## Slide 1: Tiered-Latency DRAM: A Low Latency and A Low Cost DRAM Architecture
Donghyuk Lee, Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian, Onur Mutlu
Notes: Hello. My name is Donghyuk Lee.
Today, I will talk about Tiered-Latency DRAM, which enables low latency with low cost.
This work is done in collaboration with Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian and my advisor, Onur Mutlu.
All from Carnegie Mellon University

## Slide 2: Executive Summary
Problem: DRAM latency is a critical performance bottleneck
Our Goal: Reduce DRAM latency with low area cost
Observation: Long bitlines in DRAM are the dominant source of DRAM latency
Key Idea: Divide long bitlines into two shorter segments
  Fast and slow segments
Tiered-latency DRAM: Enables latency heterogeneity in DRAM
  Can leverage this in many ways to improve performance and reduce power consumption
Results: When the fast segment is used as a cache to the slow segment  Significant performance improvement (>12%) and power reduction (>23%) at low area cost (3%)
Notes: First, let me summarize our work.
The problem is that DRAM latency is a critical bottleneck for system performance.
Our goal is to reduce the DRAM latency with low cost.
Our observation is that long bitlines are the dominant source of high DRAM latency.
Our key idea is to divide the long bitlines into two smaller segments: a fast segment and a slow segment
Therefore, our proposed DRAM architecture, Tiered-latency DRAM, enables latency heterogeneity in DRAM.
There can be many ways to utilize this latency heterogeneity to improve system performance and power reduction.
Among them, In this talk, we show that a system that uses the fast segment as a cache to the slow segment achieves significant performance improvement and power reduction with low cost for both single and multi core workloads.

## Slide 3: Outline
Motivation & Key Idea
Tiered-Latency DRAM
Leveraging Tiered-Latency DRAM
Evaluation Results
Notes: Now let me introduce the motivation and our key idea.

## Slide 4
Historical DRAM Trend
Chart: Year
| 2000 | 2003 | 2006 | 2008 | 2011
Capacity | 0.125 | 0.25 | 0.5 | 1 | 2
Latency (tRC) | 65 | 60 | 57.5 | 49.5 | 47.91
16X
-20%
DRAM latency continues to be a critical bottleneck
Notes: The figure shows the historical trends of DRAM during the last 12-years, from 2000 to 2011.
We can see that, during this time, DRAM capacity has increased by 16 times.
On the other hand, during the same period of time, DRAM latency has reduced by only 20%.
As a result, the high DRAM latency continues to be a critical bottleneck for system performance.

## Slide 5: What Causes the Long Latency?
DRAM Latency = Subarray Latency + I/O Latency
DRAM Chip
channel
cell array
I/O
DRAM Chip
channel
I/O
subarray
DRAM Latency = Subarray Latency + I/O Latency
Dominant
Subarray
I/O
Notes: To understand what causes the long latency, let me take a look at the DRAM organization.
DRAM consists of two components, the cell array and the I/O circuitry. The cell array consists of multiple subarrays.
To read from a DRAM chip, the data is first accessed from the subarray and then the data is transferred over the channel by the I/O circuitry.
So, the DRAM latency is the sum of the subarray latency and the I/O latency.
We observed that the subarray latency is much higher than the I/O latency.
As a result, subarray is the dominant source of the DRAM latency as we explained in the paper.

## Slide 6: Why is the Subarray So Slow?
Subarray
Bitline: 512 cells
extremely large sense amplifier
(≈100X the cell size)
capacitor
access
transistor
wordline
bitline
Cell
Row decoder
Sense amplifier
Long Bitline: Amortize sense amplifier → Small area
Long Bitline: Large bitline cap. → High latency
cell
Notes: To understand why the subarray is so slow, let me take a look at the subarray organization.
A subarray consists of a two-dimensional grid of cells.
Each cell consists of one capacitor and one access transistor.
The cell’s capacitor is small and can store only a small amount of charge.
That is why a subarray also has sense-amplifiers,
which are specialized circuits that can detect the small amount of charge.
Unfortunately, a sense-amplifier size is about *100* times the cell size.
So, to amortize the area of the sense-amplifiers,
hundreds of cells share the same sense-amplifier through a long bitline.
However, a long bitline has a large capacitance that increases latency.
Therefore, the long bitline is the dominant source of high DRAM latency.

## Slide 7: Trade-Off: Area (Die Size) vs. Latency
Faster
Smaller
Short Bitline
Long Bitline
Trade-Off: Area vs. Latency
Notes: A naïve way to reduce the DRAM latency is to have short bitlines that have lower latency.
Unfortunately, short bitlines significantly increase the DRAM area.
Therefore, the bitline length exposes an important trade-off between area and latency.

## Slide 8: Trade-Off: Area (Die Size) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.617764350044659 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Commodity DRAM
Long Bitline
Cheaper
Faster
Fancy DRAM
Short Bitline
GOAL
Notes: This figure shows the trade-off between DRAM area and latency as we change the bitline length.
Y-axis is the normalized DRAM area compared to a DRAM using 512 cells/bitline. A lower value is cheaper.
X-axis shows the latency in terms of tRC, an important DRAM timing constraint. A lower value is faster.
Commodity DRAM chips use long bitlines to minimize area cost. On the other hand, shorter bitlines achieve lower latency at higher cost.
Our goal is to achieve the best of both worlds: low latency and low area cost.

## Slide 9: Approximating the Best of Both Worlds
Short Bitline
Low Latency
Long Bitline
Small Area
Long Bitline
Low Latency
Short Bitline
Our Proposal
Small Area
Short Bitline  Fast
Need Isolation
Add Isolation Transistors
High Latency
Large Area
Notes: To sum up, both long and short bitline do not achieve small area and low latency.
Long bitline has small area but has high latency while short bitline has low latency but has large area.
To achieve the best of both worlds, we first start from long bitline, which has small area.
After that, to achieve the low latency of short bitline, we divide the long bitline into two smaller segments.
The bitline length of the segment nearby the sense-amplifier is same as the length of short bitline.
Therefore, the latency of the segment is as low as the latency of the short bitline.
To isolate this fast segment from the other segment, we add isolation transistors that selectively connect the two segments.

## Slide 10: Approximating the Best of Both Worlds
Low Latency
Our Proposal
Small Area
Long Bitline
Small Area
Long Bitline
High Latency
Short Bitline
Low Latency
Short Bitline
Large Area
Tiered-Latency DRAM
Low Latency
Small area using long bitline
Notes: This way, our proposed approach achieves small area and low latency.
We call this new DRAM architecture as Tiered-Latency DRAM

## Slide 11: Outline
Motivation & Key Idea
Tiered-Latency DRAM
Leveraging Tiered-Latency DRAM
Evaluation Results
Notes: Now, I will introduce Tiered-latency DRAM.

## Slide 12: Tiered-Latency DRAM
Near Segment
Far Segment
Isolation Transistor
Divide a bitline into two segments with an isolation transistor
Sense Amplifier
Notes: Again, the key idea is to divide a subarray into two segments with isolation transistors.
The segment, directly connected to the sense amplifier, is called the near segment.
The other segment is called the far segment.

## Slide 13: Near Segment Access
Far Segment
Far Segment
Near Segment
Isolation Transistor
Turn off the isolation transistor
Isolation Transistor (off)
Sense Amplifier
Reduced bitline capacitance
 Low latency & low power
Reduced bitline length
Notes: When accessing the near segment, the isolation transistor is truned off such that the near segment is electrically decoupled from the far segment.
which leads to the reduced bitline length, which leads to reduced bitline capacitance.
Due to these two reasons, the near segment can be accessed with low latency and low power.

## Slide 14: Far Segment Access
Near Segment
Near Segment
Turn on the isolation transistor
Far Segment
Isolation Transistor
Isolation Transistor (on)
Sense Amplifier
Large bitline capacitance
Additional resistance of isolation transistor
Long bitline length
 High latency & high power
Notes: When accessing the far segment, the isolation transistor is turned on
such that the far segment is electrically connected to the sense amplifier
and the entire bitline is exposed to sense amplifier,
which leads to long bitline,
which leads to large bitline capacitance.
and also isolation transistors have resistance.
Due to these three reasons, accessing the far segment incurs high latency and high power.

## Slide 15: Latency, Power, and Area Evaluation
Commodity DRAM: 512 cells/bitline
TL-DRAM: 512 cells/bitline
  Near segment: 32 cells
  Far segment: 480 cells
Latency Evaluation
  SPICE simulation using circuit-level DRAM model
Power and Area Evaluation
  DRAM area/power simulator from Rambus
  DDR3 energy calculator from Micron
Notes: We evaluated the latency, power consumption and area cost of TL-DRAM compared to commodity DRAM.
In our evaluations, we modeled a Commodity DRAM that has 512 cells/bitline.
TL-DRAM also has a total of 512 cells/bitline, which is segmented to 32-cell near segment and 480-cell far segment.
We simulated latency using SPICE simulator with circuit-level DRAM model.
We estimated the area and power consumption using Micron DRAM Power calculator and Rambus DRAM Area/Power simulator

## Slide 16: Commodity DRAM vs. TL-DRAM
Chart: 
| commodity DRAM | near segment | far segment
Normalized Power Consumption | 1 | 0.49 | 1.49
Chart: 
| commodity DRAM | near segment | far segment
Latency | 1 | 0.56 | 1.23
Latency
Power
  –56%
  +23%
  –51%
  +49%
DRAM Latency (tRC)
DRAM Power
DRAM Area Overhead
  ~3%: mainly due to the isolation transistors
  TL-DRAM
  Commodity DRAM
  Near Far
  Commodity DRAM
  Near Far
  TL-DRAM
  (52.5ns)
Notes: This figure compares the latency.
Y-axis is normalized latency.
Compared to commodity DRAM, TL-DRAM’s near segment has 56% lower latency, while the far segment has 23% higher latency.
The right figure compares the power.
Y-axis is normalized power.
Compared to commodity DRAM, TL-DRAM’s near segment has 51% lower power consumption and the far segment has 49% higher power consumption.
Lastly, mainly due to the isolation transistor, Tiered-latency DRAM increases the die-size by about 3%.

## Slide 17: Latency vs. Near Segment Length
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | Near Segment Length (Cells) | Ref.
Near Segment | 21.5788 | 21.6222 | 21.7276 | 21.9379 | 22.3353 | 23.1073 | 24.6178 | 27.8312 | 35.4616 | 52.5
Far Segment | 66.5641 | 66.4584 | 66.5141 | 66.3587 | 66.4293 | 65.8399 | 64.9221 | 64.0756 | 60.8401 | 52.5
Latency (ns)
Longer near segment length leads to
higher near segment latency
Notes: The figure shows the latency of the near and far segments when varying near segment length.
X-axis is near segment length and Y-axis is Latency in nano seconds.
As the figure shows, a longer near segment length leads to higher near segment latency due to the increased bitline capacitance of the near segment.

## Slide 18: Latency vs. Near Segment Length
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | Near Segment Length (Cells) | Ref.
Near Segment | 21.5788 | 21.6222 | 21.7276 | 21.9379 | 22.3353 | 23.1073 | 24.6178 | 27.8312 | 35.4616 | 52.5
Far Segment | 66.5641 | 66.4584 | 66.5141 | 66.3587 | 66.4293 | 65.8399 | 64.9221 | 64.0756 | 60.8401 | 52.5
Latency (ns)
Far segment latency is higher than
commodity DRAM latency
  Far Segment Length = 512 – Near Segment Length
Notes: For the far segment, a shorter far segment length leads to lower latency. However, the far segment latency is higher than commodity DRAM latency.

## Slide 19: Trade-Off: Area (Die-Area) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.617764350044659 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Cheaper
Faster
Near Segment
Far Segment
GOAL
Notes: Again, the figure shows the trade-off between area and latency in existing DRAM.
Unlike existing DRAM, TL-DRAM achieves low latency using the near segment while increasing the area by only 3%.
Although the far segment has higher latency than commodity DRAM, we show that efficient use of the near segment enables TL-DRAM to achieve high system performance.

## Slide 20: Outline
Motivation & Key Idea
Tiered-Latency DRAM
Leveraging Tiered-Latency DRAM
Evaluation Results
Notes: Now, let me explain how we can leverage TL-DRAM

## Slide 21: Leveraging Tiered-Latency DRAM
TL-DRAM is a substrate that can be leveraged by the hardware and/or software
Many potential uses
  Use near segment as hardware-managed inclusive cache to far segment
  Use near segment as hardware-managed exclusive cache to far segment
  Profile-based page mapping by operating system
  Simply replace DRAM with TL-DRAM
Notes: There are multiple ways to leverage the TL-DRAM substrate by hardware or software.
In this slide, I describe many such ways.
First, the near segment can be used as a hardware-managed inclusive cache to the far segment.
Second, the near segment can be used as a hardware-managed exclusive cache to the far segment.
Third, the operating system can intelligently allocate frequently-accessed pages to the near segment.
Forth mechanism is to simple replace DRAM with TL-DRAM without any near segment handling
While our paper provides detailed explanations and evaluations of first three mechanism,
in this talk, we will focus on the first approach, which is to use the near segment as a hardware managed cache for the far segment.

## Slide 22: Near Segment as Hardware-Managed Cache
subarray
TL-DRAM
I/O
cache
main
memory
Challenge 1: How to efficiently migrate a row between segments?
Challenge 2: How to efficiently manage the cache?
far segment
near segment
sense amplifier
channel
Notes: This diagram shows TL-DRAM organization.
Each subarray consists of the sense amplifier, near segment and far segment.
In this particular approach, only the far segment capacity is exposed to the operating system and the memory controller caches the frequently accessed rows in each subarray to the corresponding near segment.
This approach has two challenges.
First, how to migrate a row between segments efficiently?
Second, how to manage the near segment cache efficiently?
Let me first address first challenge.

## Slide 23: Inter-Segment Migration
Near Segment
Far Segment
Isolation Transistor
Sense Amplifier
Source
Destination
Goal: Migrate source row into destination row
Naïve way: Memory controller reads the source row byte by byte and writes to destination row byte by byte
→ High latency
Notes: Our goal is to migrate a source row in the far segment to a destination row in the near segment.
The naïve way to achieve this is that memory controller reads all the data from the source row and writes them back to the destination row.
However, this leads to high latency.

## Slide 24: Inter-Segment Migration
Our way:
  Source and destination cells share bitlines
  Transfer data from source to destination across shared bitlines concurrently
Near Segment
Far Segment
Isolation Transistor
Sense Amplifier
Source
Destination
Notes: Our observation is that cells in the source and the destination row share bitlines.
Our idea is to use these shared bitlines to transfer data from the source to the destination concurrently .
We’ll explain the migration procedure step by step.

## Slide 25: Inter-Segment Migration
Near Segment
Far Segment
Isolation Transistor
Sense Amplifier
Our way:
  Source and destination cells share bitlines
  Transfer data from source to destination across shared bitlines concurrently
Step 2: Activate destination row to connect cell and bitline
Step 1: Activate source row
Additional ~4ns over row access latency
Migration is overlapped with source row access
Notes: First, the memory controller accesses the source row in the far segment.
The isolation transistor is turned on and then the cells in the source row are connected to the bitlines.
After that, the sense amplifiers read the data of the source row.
Second, the memory controller accesses the destination row in the near segment.
Now, the cells in the destination row are also connected to the bitline.
Therefore, the data of sense amplifier are migrated to the destination row across the bitlines concurrently.
After these two steps, the all data of the source row are migrated to the destination row with low latency.
In fact, most of the migration latency is overlapped with the source row access latency.
Using SPICE simulation, we estimated that the additional migration latency over the row access latency is about 4ns.

## Slide 26: Near Segment as Hardware-Managed Cache
subarray
TL-DRAM
I/O
cache
main
memory
Challenge 1: How to efficiently migrate a row between segments?
Challenge 2: How to efficiently manage the cache?
far segment
near segment
sense amplifier
channel
Notes: Now, let me address the second challenge

## Slide 27: Three Caching Mechanisms
Time
  Caching
Time
  Baseline
Row 1
Row 1
Row 2
Row 2
Wait-inducing row
Wait until finishing Req1
Cached row
Reduced wait
  Is there another benefit of caching?
Req. for Row 1
Req. for Row 2
Req. for Row 1
Req. for Row 2
SC (Simple Caching)
  Classic LRU cache
  Benefit: Reduced reuse latency
WMC (Wait-Minimized Caching)
  Identify and cache only wait-inducing rows
  Benefit: Reduced wait
BBC (Benefit-Based Caching)
  BBC ≈ SC + WMC
  Benefit: Reduced reuse latency & reduced wait
Notes: Since the near segment is faster than the far segment, the near segment can be used as an LRU cache to the far segment.
This is our first mechanism, Simple Caching. The benefit of Simple Caching is from reduced reuse latency.
Is there other benefit of caching?
When issuing request for a row, accessing the row takes at least minimum row-cycle time (tRC).
During the access of the row, if another request is come for same bank and different row, the request should wait until finishing previous row access.
In this case, we call the previously accessed row as waiting inducing row.
By caching waiting inducing row in near segment, we can reduce the wait of subsequent request.
Our second mechanism wait minimized caching is to identify and cache such a wait inducing row.
The third mechanism, Benefit-Based Caching, takes into account the benefits of both reduced reuse latency of serving a request and the reduced wait time for the subsequent request. Please refer to our paper for more details on benefit-based caching.

## Slide 28: Outline
Motivation & Key Idea
Tiered-Latency DRAM
Leveraging Tiered-Latency DRAM
Evaluation Results
Notes: Now, I will describe our evaluation methodology and present our results.

## Slide 29: Evaluation Methodology
System simulator
  CPU: Instruction-trace-based x86 simulator
  Memory: Cycle-accurate DDR3 DRAM simulator
Workloads
  32 Benchmarks from TPC, STREAM, SPEC CPU2006
Metrics
  Single-core: Instructions-Per-Cycle
  Multi-core: Weighted speedup
Notes: We use an x86 CPU simulator and a cycle-accurate DDR3 DRAM simulator for evaluating system performance.
We use TPC, STREAM and SPEC CPU2006 benchmarks.
We use Instructions-Per-Cycle to measure single-core performance and weighted speedup to measure multi-core performance.

## Slide 30: Configurations
System configuration
  CPU: 5.3GHz
  LLC: 512kB private per core
  Memory: DDR3-1066
    1-2 channel, 1 rank/channel
    8 banks, 32 subarrays/bank, 512 cells/bitline
    Row-interleaved mapping & closed-row policy
TL-DRAM configuration
  Total bitline length: 512 cells/bitline
  Near segment length: 1-256 cells
Notes: For baseline commodity DRAM, We use DDR3-1066 which has 512 cells/bitline.
Our TL-DRAM has the same bitline length as the baseline DRAM.
We vary the near segment length from 1 to 256 cells.

## Slide 31: Single-Core: Performance & Power
Chart: 
| IPC Improvement
SC | 0.12256
WMC | 0.11316
BBC | 0.12737
Chart: 
| Normalized Power Consumption
SC | 0.76992
WMC | 0.79017
BBC | 0.76365
IPC Improvement
Normalized Power
12.7%
–23%
Using near segment as a cache improves performance and reduces power consumption
Notes: This figure shows the IPC improvement of our three caching mechanisms over commodity DRAM.
All of them improve performance and benefit-based caching shows maximum performance improvement by 12.7%.
The right figure shows the normalized power reduction of our three caching mechanisms over commodity DRAM.
All of them reduce power consumption and benefit-based caching shows maximum power reduction by 23%.
Therefore, using near segment as a cache improves performance and reduces power consumption at the cost of 3% area overhead.

## Slide 32: Single-Core: Varying Near Segment Length
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256
SC | 0.093347 | 0.10479 | 0.11184 | 0.11726 | 0.11958 | 0.12256 | 0.10751 | 0.10803 | 0.084032
WMC | 0.073021 | 0.083047 | 0.091204 | 0.098117 | 0.10459 | 0.11316 | 0.10892 | 0.10873 | 0.086014
BBC | 0.093347 | 0.10165 | 0.10949 | 0.11549 | 0.12116 | 0.12737 | 0.11331 | 0.1091 | 0.08597
By adjusting the near segment length, we can trade off cache capacity for cache latency
Larger cache capacity
Higher caching latency
Maximum IPC Improvement
Notes: This figure shows the performance improvement over commodity DRAM, when varying the near segment length.
X-axis is the near segment length and Y-axis is the IPC improvement over commodity DRAM.
Increasing the near segment length enables larger cache capacity but the trade-off is increasing the caching latency.
As a result, the peak performance improvement is at 32 cells/bitline.
We observe that by adjusting the near segment length, we can trade off cache capacity for cache latency.

## Slide 33: Dual-Core Evaluation
We categorize single-core benchmarks into two categories
  Sens: benchmarks whose performance is sensitive to near segment capacity
  Insens: benchmarks whose performance is insensitive to near segment capacity
Dual-core workload categorization
  Sens/Sens
  Sens/Insens
  Insens/Insens
Notes: We categorize our benchmarks into two categories,
sensitive, which consists of benchmarks that are sensitive to near segment capacity and
Insensitive, which consists of benchmarks whose performance is not sensitive to near segment capacity.
We generate dual-core workloads that are sensitive/sensitive, sensitive/insensitive and insensitive/insenstive.

## Slide 34: Dual-Core: Sens/Sens
Chart: 
| 16 | 32 | 64 | 128
SC | 0.026373 | 0.03762 | 0.068551 | 0.11183
WMC | 0.019601 | 0.050626 | 0.11246 | 0.16251
BBC | 0.048098 | 0.080152 | 0.11846 | 0.1681
Performance Improv.
BBC/WMC show more perf. improvement
Near segment length (cells)
Larger near segment capacity leads to higher performance improvement in sensitive workloads
Notes: This figure shows the performance improvement of sensitive-sensitive workloads.
X-axis is near-segment length and Y-axis is weighted speed improvement over commodity DRAM.
The results shows that larger near segment capacity leads to higher performance improvement for these workloads.
Furthermore, benefit-based caching and weight-minimizing caching show more performance improvement for these workloads than simple caching.

## Slide 35: Dual-Core: Sens/Insens & Insens/Insens
Chart: 
| 16 | 32 | 64 | 128
SC | 0.11731 | 0.11986 | 0.10966 | 0.1032
WMC | 0.10995 | 0.12255 | 0.10822 | 0.10295
BBC | 0.12134 | 0.12615 | 0.10986 | 0.10319
Using near segment as a cache provides high performance improvement regardless of near segment capacity
Performance Improv.
Notes: This figure shows the performance improvement of the other two categories of workloads, sensitive-insensitive and insensitive-insensitive.
Again, X-axis is near-segment length and Y-axis is weighted speedup improvement over commodity DRAM.
The results show that using near segment as a cache provide high performance improvement regardless of near segment capacity for these workloads.

## Slide 36: Other Mechanisms & Results in Paper
More mechanisms for leveraging TL-DRAM
  Hardware-managed exclusive caching mechanism
  Profile-based page mapping to near segment
  TL-DRAM improves performance and reduces power consumption with other mechanisms
More than two tiers
  Latency evaluation for three-tier TL-DRAM
Detailed circuit evaluation for DRAM latency and power consumption
  Examination of tRC and tRCD
Implementation details and storage cost analysis in memory controller
Notes: In our paper, we provide more mechanisms and results.
First, we provide detailed explanations and evaluations of two other mechanisms,
a hardware managed exclusive caching and a profile-based OS page mapping.
Second, We provide latency evaluation for three-tier TL-DRAM.
Third, we provide detailed circuit evaluation for DRAM latency and power consumption.
Forth, we provide implementation details and storage cost analysis in memory controller.

## Slide 37: Conclusion
Problem: DRAM latency is a critical performance bottleneck
Our Goal: Reduce DRAM latency with low area cost
Observation: Long bitlines in DRAM are the dominant source of DRAM latency
Key Idea: Divide long bitlines into two shorter segments
  Fast and slow segments
Tiered-latency DRAM: Enables latency heterogeneity in DRAM
  Can leverage this in many ways to improve performance and reduce power consumption
Results: When the fast segment is used as a cache to the slow segment  Significant performance improvement (>12%) and power reduction (>23%) at low area cost (3%)
Notes: Let me conclude.
The problem is that DRAM latency is a critical bottleneck for system performance.
Our goal is to reduce the DRAM latency with low cost.
Our observation is that long bitlines are the dominant source of high DRAM latency.
Our key idea is to divide the long bitlines into two smaller segments: a fast segment and a slow segment
Therefore, Tiered-latency DRAM, enables latency heterogeneity in DRAM.
We show many ways to utilize this latency heterogeneity to improve system performance and power reduction.
Among them, In this talk, we show that a system that uses the fast segment as a cache to the slow segment achieves significant performance improvement and power reduction with low cost for wide variety of both single and multi core workloads.

## Slide 38
Thank You
Notes: Thank you

## Slide 39: Tiered-Latency DRAM: A Low Latency and A Low Cost DRAM Architecture
Donghyuk Lee, Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian, Onur Mutlu
Notes: I’m happy to take any question.

## Slide 40
Backup Slides

## Slide 41: Storage Cost in Memory Controller
Organization
  Bitline Length: 512 cells/bitline
  Near Segment Length: 32 cells
  Far Segment Length: 480 cells
  Inclusive Caching
Simple caching and wait-minimized caching
  Tag Storage: 9 KB
  Replace Information: 5 KB
Benefit-based caching
  Tag storage: 9 KB
  Replace Information: 8 KB (8 bit benefit field/near segment row)

## Slide 42: Hardware-managed Exclusive Cache
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Performance Improvement | 0.079 | 0.082 | 0.099274
Power Reduction | 0.093589 | 0.11826 | 0.14278
Near and Far segment: Main memory
Caching: Swapping near and far segment row
  Need one dummy row to swap
Performance improvement is lower than Inclusive caching due to high swapping latency
7.2%
8.9%
9.9%
9.4%
11.4%
14.3%

## Slide 43: Profile-Based Page Mapping
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Performance Improvement | 0.08849 | 0.11597 | 0.071916
Power Reduction | 0.1921 | 0.2484 | 0.2142
Operating system profiles applications and maps frequently accessed rows to the near segment
Allocating frequently accessed rows in the near segment provides performance improvement
8.9%
11.6%
7.2%
19%
24.8%
21.5%

## Slide 44: Three-Tier Analysis
Three tiers
  Add two isolation transistors
  Near/Mid/Far segment length: 32/224/256 Cells
More tiers enable finer-grained caching and partitioning mechanisms
Chart: 
| Baseline | Near Segment | Middle Segment | Far Segment
Latency | 1 | 0.44 | 0.778 | 1.569
Latency
  –56%
  Three-Tier TL-DRAM
  Commodity DRAM
  Near Mid Far
  –23%
  57%