## Slide 1
Metadata cache
Avoids additional requests to metadata
Memory bandwidth reduction
Zero pages and zero cache lines
Main memory is a limited shared resource
Observation: Significant data redundancy
Idea: Compress data in main memory
Problem: How to avoid latency increase?
Solution: Linearly Compressed Pages (LCP):
fixed-size cache line granularity compression
1. Increases capacity (62% on average)
2. Decreases bandwidth consumption (24%)
3. Improves overall performance (13.9%)
4. Decreases memory energy consumption (9.5%)
Summary
Linearly Compressed Pages (LCP)
LCP Overview
Key Results: Compression Ratio, Performance, Page Faults
L0
L1
L2
. . .
LN-1
Cache Line (64B)
Uncompressed Page
Address Offset
0
64
128
(N-1)*64
L0
L1
L2
. . .
LN-1
Compressed Page
Address Offset
0
?
?
?
Challenge: Address Computation
SPEC2006, databases, web workloads, L2 2MB cache
No. | Label | Description
1 | Baseline | Baseline (no compression)
2 | RMC-FPC | Main memory compression using RMC and FPC
3 | LCP-FPC | LCP framework with FPC
4 | LCP-BDI | LCP framework with BDI
5 | MXT | IBM MXT design
Evaluated designs
64B
Uncompressed Page (4KB: 64*64B)
64B
64B
64B
. . .
64B
. . .
Compressed Data
(1KB)
M
E
Metadata (64B):
? (compressible) and
? (zero cache line)
Exception
Storage
4:1 Compression
LCP Optimizations
Page Table entry extension
compression type, size, and extended physical base address
Operating System management support
4 memory pools (512B, 1KB, 2KB, 4KB)
Handling page overflows
Hardware support
Compression algorithms:
Base-Delta-Immediate (BDI) and
Frequent Pattern Compression (FPC)
64B
64B
64B
64B
4 cache lines in 1 transfer
Handled separately in TLB (1-bit) and metadata (1-bit per line )
4 memory transfers
Linearly Compressed Pages: A Low Complexity, Low Latency
Main Memory Compression Framework
G. Pekhimenko, V. Seshadri, Y. Kim, H. Xin, O. Mutlu, T. C. Mowry (CMU), P. B. Gibbons, M. A. Kozuch (Intel Labs)
Chart: GeoMean
| GeoMean
Baseline | 1
RMC-FPC | 1.5908
LCP-FPC | 1.5193
LCP-BDI | 1.6239
MXT | 2.3051
MICRO 2013, Davis, CA
Challenge in Memory Compression
Methodology
Chart: Cores
| 1 | 2 | 4
RMC-FPC | 0.023 | 0.057 | 0.043
LCP-FPC | 0.05 | 0.093 | 0.078
LCP-BDI | 0.061 | 0.139 | 0.107
Chart: DRAM Size
| 256MB | 512MB | 768MB | 1GB
Baseline | 1 | 0.82646 | 0.73241 | 0.60882
LCP-BDI | 0.92234 | 0.71333 | 0.56312 | 0.48679