## Slide 1: Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency
Gennady Pekhimenko,
Vivek Seshadri , Yoongu Kim, Hongyi Xin, Onur Mutlu,
Todd C. Mowry
Phillip B. Gibbons,
Michael A. Kozuch

## Slide 2: Executive Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Idea: Compress data in main memory
Problem: How to avoid inefficiency in address computation?
Solution: Linearly Compressed Pages (LCP):
fixed-size cache line granularity compression
Increases memory capacity (62% on average)
Decreases memory bandwidth consumption (24%)
Decreases memory energy consumption (4.9%)
Improves overall performance (13.9%)

## Slide 3: Potential for Data Compression
Significant redundancy in in-memory data:
0x00000000
How can we exploit this redundancy?
  Main memory compression helps
  Provides effect of a larger memory without making it physically larger
0x0000000B
0x00000003
0x00000004
…

## Slide 4: Challenges in Main Memory Compression
Address Computation
Mapping and Fragmentation

## Slide 5: Challenge 1: Address Computation
L0
L1
L2
. . .
LN-1
Cache Line (64B)
Address Offset
0
64
128
(N-1)*64
L0
L1
L2
. . .
LN-1
Compressed Page
0
?
?
?
Address Offset
Uncompressed Page
Notes: Talk about the last cache line

## Slide 6: Challenge 2: Mapping & Fragmentation
Virtual Page
(4KB)
Physical Page
(? KB)
Fragmentation
Virtual
Address
Physical
Address

## Slide 7: Outline
Motivation & Challenges
Shortcomings of Prior Work
LCP: Key Idea
LCP: Implementation
Evaluation
Conclusion and Future Work

## Slide 8: Key Parameters in Memory Compression
Compression Ratio | Address Comp. Latency | Decompression Latency | Complexity and Cost

## Slide 9: Shortcomings of Prior Work
Compression Mechanisms | Compression Ratio | Address Comp. Latency | Decompression Latency | Complexity and Cost
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
2X
64 cycles
Notes: Doubling the memory access latency
64 processor cycles
Complex 32 MB LLC with 1KB cache blocks

## Slide 10: Shortcomings of Prior Work (2)
Compression Mechanisms | Compression Ratio | Address Comp. Latency | Decompression Latency | Complexity And Cost
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 
Notes: More details on complexity and cost

## Slide 11: Shortcomings of Prior Work (3)
Compression Mechanisms | Compression Ratio | Address Comp. Latency | Decompression Latency | Complexity And Cost
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 
LCP: Our Proposal |  |  |  | 
Notes: Address computation latency – hidden, but leads to high energy cost

## Slide 12: Linearly Compressed Pages (LCP): Key Idea
64B
64B
64B
64B
. . .
. . .
4:1 Compression
64B
Uncompressed Page (4KB: 64*64B)
Compressed Data
(1KB)
LCP effectively solves challenge 1: address computation
128
32
 Fixed compressed size
Notes: In LCP, we restrict the compression algorithm to provide the same fixed compressed size for all cache lines.
The primary advantage of this restriction is that now address computation is a simple linear scaling of the cache line offset before compression.
For example, for the 3rd cache line – offset was 128, after compression with 4:1 compression – it is simply 32 bytes offset within LCP page.
The fixed-size restriction also leads to a compressed data region being fixed in size (e.g., 1KB with 4:1 compression).

## Slide 13: LCP: Key Idea (2)
4:1 Compression
E
64B
64B
64B
64B
. . .
. . .
M
Metadata
(64B)
Exception
Storage
64B
Uncompressed Page (4KB: 64*64B)
Compressed Data
(1KB)
idx
E0
Notes: Unfortunately, not all data is compressible, hence we need (1) keep exceptional cache lines in a separate exception region in the uncompressed form.
(2) a dedicated metadata region that stores (a) a bit per cache line -- to represent the fact that some cache lines are compressed and some are not, (b) as well as the corresponding index that maps to the exception storage elements occupied by the corresponding uncompressed cache line.
…

## Slide 14: But, wait …
E
64B
64B
64B
64B
. . .
. . .
M
4:1 Compression
64B
Uncompressed Page (4KB: 64*64B)
Compressed Data
(1KB)
How to avoid 2 accesses ?
 Metadata (MD) cache
Notes: Our solution to this inefficiency is MD cache. 32KB in size, located at the memory controller.
In the common case of the MD hit (more than 90% of cases), the access to the metadata is fully avoided.

## Slide 15: Key Ideas: Summary
 Fixed compressed size per cache line
 Metadata (MD) cache

## Slide 16: Outline
Motivation & Challenges
Shortcomings of Prior Work
LCP: Key Idea
LCP: Implementation
Evaluation
Conclusion and Future Work

## Slide 17: LCP Overview
Page Table entry extension
  compression type and size (fixed encoding)
OS support for multiple page sizes
  4 memory pools (512B, 1KB, 2KB, 4KB)
Handling uncompressible data
Hardware support
  memory controller logic
  metadata (MD) cache
PTE
512B
1KB
2KB
4KB

## Slide 18: Page Table Entry Extension
c-bit (1b)
c-type (3b)
Page Table Entry
c-size (2b)
c-base (3b)
c-bit (1b) – compressed or uncompressed page
c-type (3b) – compression encoding used
c-size (2b) – LCP size (e.g., 1KB)
c-base (3b) – offset within a page

## Slide 19: Physical Memory Layout
1
4
4KB
2KB
2KB
1KB
1KB
1KB
1KB
512B
512B
...
512B
4KB
…
…
Page Table
PA1
PA2
…
PA2 + 512*1
PA1 + 512*4
PA0
Notes: 512 bytes – minimum page size

## Slide 20: Memory Request Flow
Initial Page Compression
Cache Line Read
Cache Line Writeback

## Slide 21: Memory Request Flow (2)
Initial Page Compression (1/3)
Last-Level
Cache
Core
TLB
Compress/ Decompress
Memory
Controller
MD Cache
Processor
Disk
DRAM
4KB
1KB
1. Initial Page Compression
2. Cache Line Read
LD
LD
1KB
$Line
3. Cache Line Writeback
$Line
2KB
$Line
Cache Line Read (2/3)
Cache Line Writeback (3/3)
Notes: What Metadata has in it?
MD Cache is the common case

## Slide 22: Handling Page Overflows
Happens after writebacks, when all slots in the exception storage are already taken
Two possible scenarios:
  Type-1 overflow: requires larger physical page size (e.g., 2KB instead of 1KB)
  Type-2 overflow: requires decompression and full uncompressed physical page (e.g., 4KB)
…
$ line
M
Compressed Data
E0
Exception Storage
E1
E2
Happens infrequently -
once per ~2M instructions

## Slide 23: Compression Algorithms
Key requirements:
  Low hardware complexity
  Low decompression latency
  High effective compression ratio
Frequent Pattern Compression [ISCA’04]
  Uses simplified dictionary-based compression
Base-Delta-Immediate Compression [PACT’12]
  Uses low-dynamic range in the data

## Slide 24: Base-Delta Encoding [PACT’12]
32-byte Uncompressed Cache Line
0xC04039C0
0xC04039C8
0xC04039D0
…
0xC04039F8
0xC04039C0
Base
0x00
1 byte
0x08
1 byte
0x10
1 byte
…
0x38
12-byte
Compressed Cache Line
  20 bytes saved
   Fast Decompression: vector addition
   Simple Hardware:
  arithmetic and comparison
   Effective: good compression ratio
BDI [PACT’12] has two bases:
zero base (for narrow values)
arbitrary base (first non-zero value in the cache line)
Notes: Mention real application – mcf
This is the basic idea behind BDI

## Slide 25: LCP-Enabled Optimizations
Memory bandwidth reduction:
Zero pages and zero cache lines
  Handled separately in TLB (1-bit) and in metadata
  (1-bit per cache line)
64B
64B
64B
64B
1 transfer
instead of 4

## Slide 26: Outline
Motivation & Challenges
Shortcomings of Prior Work
LCP: Key Idea
LCP: Implementation
Evaluation
Conclusion and Future Work

## Slide 27: Methodology
Simulator: x86 event-driven based on Simics
Workloads (32 applications)
  SPEC2006 benchmarks, TPC, Apache web server
System Parameters
  L1/L2/L3 cache latencies from CACTI [Thoziyoor+, ISCA’08]
  512kB - 16MB L2 caches
  DDR3-1066, 1 memory channel
Metrics
  Performance: Instructions per cycle, weighted speedup
  Capacity: Effective compression ratio
  Bandwidth: Bytes per kilo-instruction (BPKI)
  Energy: Memory subsystem energy

## Slide 28: Evaluated Designs
Design | Description
Baseline | Baseline (no compression)
RMC | Robust main memory compression[ISCA’05] (RMC) and FPC[ISCA’04]
LCP-FPC | LCP framework with FPC
LCP-BDI | LCP framework with BDI[PACT’12]
LZ | Lempel-Ziv compression (per page)

## Slide 29: Effect on Memory Capacity
32 SPEC2006, databases, web workloads, 2MB L2 cache
LCP-based designs achieve competitive average compression ratios with prior work
Chart: Compression Ratio
| GeoMean
Baseline | 1
RMC | 1.5908
LCP-FPC | 1.5193
LCP-BDI | 1.6239
LZ | 2.6

## Slide 30: Effect on Bus Bandwidth
32 SPEC2006, databases, web workloads, 2MB L2 cache
LCP-based designs significantly reduce bandwidth (24%)
(due to data compression)
Better
Chart: Normalized BPKI
| GeoMean
Baseline | 1
RMC | 0.78679
LCP-FPC | 0.79521
LCP-BDI | 0.75692

## Slide 31: Effect on Performance
LCP-based designs significantly improve performance over RMC
Chart: Performance Improvement
| 1-core | 2-core | 4-core
RMC | 0.023 | 0.057 | 0.043
LCP-FPC | 0.05 | 0.093 | 0.078
LCP-BDI | 0.061 | 0.139 | 0.107

## Slide 32: Effect on Memory Subsystem Energy
32 SPEC2006, databases, web workloads, 2MB L2 cache
LCP framework is more energy efficient than RMC
Better
Chart: Normalized Energy
| GeoMean
Baseline | 1
RMC | 1.0611
LCP-FPC | 0.96635
LCP-BDI | 0.94756

## Slide 33: Effect on Page Faults
32 SPEC2006, databases, web workloads, 2MB L2 cache
LCP framework significantly decreases the number of page faults (up to 23% on average for 768MB)
Chart: DRAM Size
| 256MB | 512MB | 768MB | 1GB
Baseline | 1 | 0.82646 | 0.73241 | 0.60882
LCP-BDI | 0.92234 | 0.71333 | 0.56312 | 0.48679

## Slide 34: Other Results and Analyses in the Paper
Analysis of page overflows
Compressed page size distribution
Compression ratio over time
Number of exceptions (per page)
Detailed single-/multicore evaluation
Comparison with stride prefetching
  performance and bandwidth

## Slide 35: Conclusion
Old Idea: Compress data in main memory
Problem: How to avoid inefficiency in address computation?
Solution: A new main memory compression framework called LCP (Linearly Compressed Pages)
  Key idea: ﬁxed-size for compressed cache lines within a page
Evaluation:
  Increases memory capacity (62% on average)
  Decreases bandwidth consumption (24%)
  Decreases memory energy consumption (4.9%)
  Improves overall performance (13.9%)

## Slide 36: Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency
Gennady Pekhimenko,
Vivek Seshadri , Yoongu Kim, Hongyi Xin, Onur Mutlu,
Todd C. Mowry
Phillip B. Gibbons,
Michael A. Kozuch

## Slide 37: Backup Slides

## Slide 38: Large Pages (e.g., 2MB or 1GB)
Splitting large pages into smaller 4KB sub-pages (compressed individually)
64-byte metadata chunks for every sub-page
2KB
2KB
…
2KB
2KB
M

## Slide 39: Physically Tagged Caches
Core
TLB
tag
tag
tag
Physical Address
data
data
data
Virtual
Address
Critical Path
Address Translation
L2 Cache
Lines

## Slide 40: Changes to Cache Tagging Logic
Before:
tag
tag
p-base
data
data
data
Cache
Lines
tag
p-base – physical page base address
c-idx – cache line index within the page
After:
p-base
c-idx

## Slide 41: Analysis of Page Overflows
Chart: 
| apache | astar | bzip2 | cactusADM | gcc | GemsFDTD | gromacs | h264ref | lbm | leslie3d | libquantum | mcf | omnetpp | perlbench | sjeng | soplex | sphinx3 | tpcc | tpch6 | xalancbmk | zeusmp | GeoMean
 | 1.433e-05 | 1.11e-06 | 5.04e-06 | 4.49e-06 | 5.2e-07 | 1e-08 | 1e-08 | 1.7e-07 | 1e-08 | 8e-08 | 1e-08 | 2.2e-07 | 7.35e-07 | 6e-07 | 1.21e-06 | 2.3475e-05 | 4.99e-06 | 5.81e-06 | 1.64e-05 | 2.5e-07 | 1.885e-06 | 4.7776e-07

## Slide 42: Frequent Pattern Compression
Idea: encode cache lines based on frequently occurring patterns, e.g., first half of a word is zero
0x00000001
0x00000000
0xFFFFFFFF
0xABCDEFFF
0x00000001
001
0x00000000
000
0xFFFFFFFF
011
0xABCDEFFF
111
Frequent Patterns:
000 – All zeros
001 – First half zeros
010 – Second half zeros
011 – Repeated bytes
100 – All ones
…
111 – Not a frequent pattern
001
0x0001
000
011
0xFF
111
0xABCDEFFF
0x0001
0xFF
0xABCDEFFF

## Slide 43: GPGPU Evaluation
Gpgpu-sim v3.x
Card: NVIDIA GeForce GTX 480 (Fermi)
Caches:
  DL1: 16 KB with 128B lines
  L2: 786 KB with 128B lines
Memory: GDDR5

## Slide 44: Effect on Bandwidth Consumption
Chart: Normalized BPKI
| BFS | MUM | JPEG | NN | LPS | STO | CONS | SCP | spmv | sad | backprop | hotspot | streamcluster | PVC | PVR | InvIdx | SS | bfs | bh | dmr | mst | sp | sssp | GeoMean | CUDA | Parboil | Rodinia | Mars | Lonestar
BDI | 2.16 | 1.45 | 1.74 | 1.34 | 1.81 | 1.42 | 1.17 | 1.33 | 2.28 | 1.15 | 1.17 | 1.66 | 1.34 | 2.29 | 1.65 | 1.37 | 1.72 | 2.95 | 1.52 | 1.44 | 1.62 | 1.45 | 2.28 | 1.615
LCP-BDI | 1.45 | 1.37 | 1.45 | 1.26 | 1.42 | 1.31 | 1.17 | 1.33 | 1.65 | 1.1 | 1.16 | 1.36 | 1.33 | 1.6 | 1.35 | 1.34 | 1.38 | 1.82 | 1.34 | 1.36 | 1.34 | 1.33 | 1.67 | 1.3773

## Slide 45: Effect on Throughput
Chart: Normalized Performance
| BFS | MUM | JPEG | NN | LPS | STO | CONS | SCP | spmv | sad | backprop | hotspot | streamcluster | PVC | PVR | InvIdx | SS | bfs | bh | dmr | mst | sp | sssp | GeoMean | CUDA | Parboil | Rodinia | Mars | Lonestar
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
BDI | 1.0079 | 1.301 | 1.1874 | 1 | 1.2313 | 1.0092 | 1.1179 | 1.2534 | 1.0877 | 1.0014 | 1.0012 | 1.0154 | 1.0354 | 1.8231 | 1.4028 | 1.0029 | 1.2631 | 1.0681 | 1.0574 | 1.0009 | 1.3603 | 1.2812 | 1.1029 | 1.1436

## Slide 46: Physical Memory Layout
1
4
4KB
2KB
2KB
1KB
1KB
1KB
1KB
512B
512B
...
512B
4KB
…
…
Page Table
PA1
c-base
PA2
…
PA2 + 512*1
PA1 + 512*4
PA0
Notes: 512 bytes – minimum page size

## Slide 47: Page Size Distribution

## Slide 48: Compression Ratio Over Time

## Slide 49: IPC (1-core)

## Slide 50: Weighted Speedup

## Slide 51: Bandwidth Consumption

## Slide 52: Page Overflows

## Slide 53: Stride Prefetching - IPC

## Slide 54: Stride Prefetching - Bandwidth

## Slide 55: Future Work
LCP + prefetching
  Use prefetching as a “hint” producer to detect locality
  LCP feedback: don’t generate prefetch requests to the cache lines LCP can bring for free (adaptive)
  LCP dynamic restructuring based on spatial pattern information
GPU evaluation
  New compressed memory designs
  New compression algorithms