## Slide 1: Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency
Gennady Pekhimenko,
Vivek Seshadri , Yoongu Kim, Hongyi Xin, Onur Mutlu,
Todd C. Mowry
Phillip B. Gibbons,
Michael A. Kozuch

## Slide 2: Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Old Idea: Compress data in main memory
Problem: How to avoid inefficiency in address computation?
Solution: Linearly Compressed Pages (LCP): fixed-size cache line granularity compression
1. Increases capacity (62% on average)
2. Decreases bandwidth consumption (24%)
3. Improves overall performance (13.9%)

## Slide 3: Linearly Compressed Pages (LCP)
64B
64B
64B
64B
. . .
. . .
M
E
Metadata (64B): ? (compressible)
Exception
Storage
4:1 Compression
64B
Uncompressed Page (4kB: 64*64B)
Compressed
Data (1kB)