## Slide 1
Linearly Compressed Pages: A Main Memory Compression Framework
with Low Complexity and Low Latency
Gennady Pekhimenko, Advisers: Todd C. Mowry and Onur Mutlu (Carnegie Mellon University)
Executive Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Idea: Compress data in main memory
Problem: How to avoid latency increase?
Solution: Linearly Compressed Pages (LCP):
fixed-size cache line granularity compression
1. Increases capacity (69% on average)
2. Decreases bandwidth consumption (46%)
3. Improves overall performance (9.5%)
Challenges in Main Memory Compression
Linearly Compressed Pages (LCP): Key Idea
LCP Overview
Key Results: Compression Ratio, Bandwidth, Performance
References
L0
L1
L2
. . .
LN-1
Cache Line (64B)
Uncompressed Page
Address Offset
0
64
128
(N-1)*64
L0
L1
L2
. . .
LN-1
Compressed Page
Address Offset
0
?
?
?
Challenge 1: Address Computation
Virtual Page
(4kB)
Virtual
Address
Physical Page
(? kB)
Physical
Address
Fragmentation
Challenge 2: Mapping and Fragmentation
Core
TLB
On-Chip Cache
Cache Lines
tag
tag
tag
Physical Address
data
data
data
Virtual
Address
Challenge 3: Physically Tagged Caches
Critical Path
Chart: GeoMean
| GeoMean
Zero Page | 1.2982
FPC | 1.5908
LCP (BDI) | 1.6239
LCP (BDI+FPC-fixed) | 1.6909
MXT | 2.3051
LZ | 2.6049
SPEC2006, databases, web workloads, L2 2MB cache
Chart: Normalized BPKI
| GeoMean
FPC-cache | 0.92005
BDI-cache | 0.89057
FPC-memory | 0.57215
(None, LCP-BDI) | 0.62549
(FPC, FPC) | 0.5362
(BDI, LCP-BDI) | 0.55124
(BDI, LCP-BDI+FPC-fixed) | 0.53836
Cores | LCP-BDI | (BDI, LCP-BDI) | (BDI, LCP-BDI+FPC-fixed)
1 | 6.1% | 9.5% | 9.3%
2 | 13.9% | 23.7% | 23.6%
4 | 10.7% | 22.6% | 22.5%
Average performance improvement:
No. | Label: (Cache, Memory) | Description
1 | (None, None) | Baseline (no compression)
2 | FPC-Cache | LLC compression using FPC [3]
3 | BDI-Cache | LLC compression using BDI [2]
4 | FPC-Memory | Main memory compression using [1]
5 | LCP-BDI | LCP-framework with BDI
6 | (FPC, FPC) | Designs 2 and 4 combined
7 | (BDI, LCP-BDI) | Designs 3 and 5 combined
8 | (BDI, LCP-BDI+FPC-fixed) | Design 3 combined with BDI+FPC-fixed
Evaluated designs
[1] M. Ekman and P. Stenstrom. A Robust Main Memory Compression Scheme, ISCA’05
[2] G. Pekhimenko et al., Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches, PACT’12
[3] A. Alameldeen and D. Wood. Adaptive Cache Compression for High-Performance Processors, ISCA’04
[4] B. Abali et al., Memory expansion technology (MXT): software support and performance. IBM J.R.D. ’01
64B
Uncompressed Page (4kB: 64*64B)
64B
64B
64B
. . .
64B
. . .
Compressed Data
(1kB)
M
E
Metadata (64B):
? (compressible) and ? (zero cache line)
Exception
Storage
4:1 Compression
LCP Optimizations
Page Table entry extension
compression type, size, and extended physical base address
Operating System management support
4 memory pools (512B, 1kB, 2kB, 4kB)
Changes to cache tagging logic
physical page base address + cache line index (within a page)
Handling page overflows
Compression algorithms: BDI [2], FPC [3]
Metadata cache
Avoids additional requests to metadata
Memory bandwidth reduction
Zero pages and zero cache lines
64B
64B
64B
64B
4 cache lines in 1 transfer
Handled separately in TLB (1-bit) and metadata (1-bit per line )
4 memory transfers needed
Solves all 3
challenges
Address Translation