## Slide 1: A Low-Overhead, Fully-Distributed, Guaranteed-Delivery Routing Algorithm for Faulty Network-on-Chips
Mohammad Fattah1, Antti Airola1, Rachata Ausavarungnirun2, Nima Mirzaei3, Pasi Liljeberg1, Juha Plosila1, Siamak Mohammadi3, Tapio Pahikkala1, Onur Mutlu2 and Hannu Tenhunen1

## Slide 2: What is This Talk About?
Overtime, routers and links can become faulty.
Dynamically find alternative paths.
Previous works have at least one of the following limitations:
  Cover only few number of faults
  Use a central controller
  High area overhead
  High reconfiguration overhead upon new faults
Maze-Routing overcomes all the above limitations:
  Full-coverage: formally proven
  Fully-distributed: using autonomous and standalone routers
  Low area overhead: using an algorithmic approach (16X less area compared to routing tables)
  Low reconfiguration overhead: by on the fly path exploration (Instantaneous operation on new failures)
  Better performance: 50% higher saturation throughput and, 28% lower latency on SPEC benchmarks compared to state-of-the-art

Source: condenaststore.com
 Any # of faults
 Detect partitioning
 No central component
 No reconfiguration phase
 No routing table
Notes: It is almost a decade that NOC idea is around and many research has done this area so far
1- One of the main challenges of this area is technology shrinkage. As a result, devices wear out and overtime, NOC components, like routers and links, can become faulty.
In order to keep the system functioning, we need to keep the connectivity between nodes, even if some parts of the network are not working anymore.
2- One main solution to this problem is dynamic fault-tolerant routings. This very well suits the NoC nature as the path divergence comes as a free lunch.
3- There is an enormous amount of research carried out in this area. However, previous works have some serious practical limitations. I briefly introduce these limitations now. But I will go into details later on.
4- First, they may not work when there more than few number of failures. Also, some of them use a central controller to overcome the fault situation. Besides, most of them are using routing tables or other techniques which leads to high area overhead. Finally, it takes a long while for most of them to find alternative paths, and during this time, the normal operation of the network is paused.
As I said, I will go into details of each, one by one, during this talk. But as mentioned, the main point is that there is no previous work which has none of the above mentioned limitations.
Whereas, we believe in order for a fault-tolerant routing algorithm to be applicable and practical, it should overcome all of them.
5- This is our main motivation for proposing this work; we called it Maze-Routing. Our method, in contrast to previous works, has none of the above mentioned limits.
6- First, It provides full coverage, and we formally prove this. And, what do we mean by full coverage?
7- One, it can tolerate any number of faulty components.
8- And two, it indicates when a destination is not reachable anymore.
9- As the second attribute, our algorithm works in a fully distributed manner. In other words, there is no central component, and no synchronization between routers. Routers are fully autonomous with standalone decisions.
10- Third, we use no routing table; i.e. our method is an algorithmic approach. As a result, realization of our algorithm is 16 times smaller than the smallest routing table, used in previous works.
11- Fourth, routers of our method find the path to destination on the fly. So, basically, there is no reconfiguration phase and any consequent overhead. In other words, network continues its normal operation seamlessly upon new faults.
12- In addition to above mentioned attributes, our results demonstrate 50% higher saturation throughput, and 28% lower average network latency, when there are up to 5 links failed.
So, after this brief summary of the talk, now, let’s move to the details of Maze-Routing algorithm.

## Slide 3: Aggressive Transistor Scaling
Key Benefit
A Major Curse
Integrating many IPs
  Processors
  Cache slices
  Memory controllers
  Specialized HW
  Etc.
Reduced reliability
  Fabrication time:
    Defect
    Process variation
  Run-time:
    Negative bias temperature instability (NBTI)
    Hot carrier injection (HCI)
    Gate oxide breakdown
    Electro-Migration
  Our designs must be:
  Fault-tolerant by construction!

## Slide 4: IP vs. Network Faults
IP
  Degrades the performance
  Rest of the system can continue
Network Elements
  Cripples the performance
  Single point of failure


It is crucial to tolerate
Many faults in links and routers!

## Slide 5: Maze-Routing
Fault-Tolerant by Construction
Four Critical Goals
It is not:
  A router architecture, with fault tolerance patched to it
Rather, it is
  Essentially a routing algorithm, which
  Is inherently fault-tolerant
Full coverage (guaranteed delivery)
Fully-distributed operation
Low area footprint
No reconfiguration component/phase
Maze-Routing is
The first to provide all!
XY
XY
XY
XY
XY
X
Priority Arbiter
North
East
South
West
Local
North
East
South
West
Local
Maze
Maze
Maze
Maze
Maze

## Slide 6
Our 4 Goals
- Full coverage
- Full distribution
- Low area cost
- Fast adaptation
Maze-Routing
- Finding the path
- Detecting disconnected nodes
Results
- Area
- Throughput
- Reconfiguration overhead

## Slide 7
Our 4 Goals
- Full coverage
- Full distribution
- Low area cost
- Fast adaptation
Maze-Routing
> Finding the path
> Detecting disconnected nodes
Results
- Area
- Throughput
- Reconfiguration overhead

## Slide 8: Goal 1: Full (Fault) Coverage
Literature
Maze-Routing
Limited number of faults
Limited fault pattern
Limited when disconnected nodes
No restriction on
  Fault count
  Fault pattern
Detect disconnected nodes
  At router level

## Slide 9: Goal 2: Fully Distributed Operation
Literature
Maze-Routing
Centralized methods
  Single point of failure
    TMR: Expensive
Distributed methods
  Synchronization points.
  Fault in Reconf. unit.
No central component
No reconfiguration unit
Each router makes individual decisions
Faults in algorithm only disables the associated links
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Reconf.
Cent. SW/HW Controller



Maze
Maze
Maze
Maze
Maze
Maze
X
Priority Arbiter
North
East
South
West
Local
North
East
South
West
Local
Maze


## Slide 10: Goal 3: Low Area Overhead
Literature
Maze-Routing
Routing tables
  High area overhead
    5 read ports
Implementation cost
Power dissipation
Vulnerability to run-time faults
  One failed bit: affects the whole router
  Area ~ fault probability of router
An algorithmic approach
No routing table

## Slide 11: Goal 4: Low Reconfiguration Overhead
Literature
Maze-Routing
New failure detected?
  Pause the network
  Reconfigure to an alternative solution
  Resume normal operation
Issues?
  Severe degradation of performance
  aggressive online testing
Few works with fast reconfiguration
No reconfiguration phase
Path to destination is dynamically calculated per packet
Called on the fly reconfiguration

## Slide 12: Maze-Routing: The First to Provide All
 | Coverage | Reconfiguration | O(Area) | O(Reconf.)
Zhang et al. [43] | few | fully distributed | low | on the fly
LBDR [35] | moderate | central | low | N/A
d2-LBDR [7] | moderate | central | low | N/A
OSR-Lite [38] | moderate | central | low | moderate
TOSR [5] | moderate | distributed | high | fast
BLINC [25] | moderate | distributed | high | fast
uLBDR [36] | high | central | high | N/A
Wachter et al. [39] | high | distributed | high | slow
Fick et al. [19] | high | distributed | high | slow
Face routing [11] | high | fully distributed | excessive | on the fly
FTDR-H [18] | high | fully distributed | high | fast
uDIREC [32] | full | central | high | excessive
ARIADNE [3] | full | distributed | high | slow
Maze-routing | full | fully distributed | low | on the fly

## Slide 13
Our 4 Goals
- Full coverage
- Full distribution
- Low area cost
- Fast adaptation
Maze-Routing
- Finding the path
- Detecting disconnected nodes
Results
- Area
- Throughput
- Reconfiguration overhead

## Slide 14: Preliminaries
Face: regions bounded by links and routers
  4 inner faces
  1 outer face
Right/Left hand rule: exit from first output in right/left side.
  : clockwise around inner faces
  : counterclockwise around inner faces
  Opposite direction around outer faces

## Slide 15: Preliminaries (II)
Few additional fields in the header
MDbest : closest distance (MD) to dst that the packet has reached so far
  Initial: MDsrc, dst
  Only decrements
  Mode: routing mode used for the packet
  Values: normal, traversal ( or ), unreachable
  Initial: normal
2 more fields to detect disconnected nodes

## Slide 16: Maze-Routing
Normal mode:
  Is there any productive output?
    Take it and dec(MDbest)
  No? we should enter traversal mode:
    Draw line(cur, dst) between current node and dst
    ? Take the first output in the left of line(cur, dst)
    ? Take the first output in the right of line(cur, dst)
    Set the mode (either  or ), accordingly
Traversal mode:
  If MDcur, dst = MDbest with productive output?
    Return to (and act as in) normal mode
  Otherwise, follow the hand rule
5
4
3
2
4
3
2
1
3
1
4
3
2
1
dst
src
5│N
4│N
3│N
3│
2│N
1│N
0│N
Maze-Routing definitely reaches dst, if a path to dst exists.
We provide the formal proof in the paper.
Notes: 1- Explain the figure, and numbers in nodes
2- address the path divergence`

## Slide 17: Detecting Disconnected Nodes
Traversal mode:
  If MDcur, dst = MDbest with productive output?
    Return to normal mode
  No?
    Follow the hand rule
The destination is unreachable if:
  In traversal mode, we meet the same node as the one we entered the traversal mode
  The hand rule picks the same output as when we entered the traversal mode
3
2
3
4
2
1
2
3
1
1
2
2
1
2
3
dst
src
3│N
1│N
1│
More implementation details are available in the paper

## Slide 18
Our 4 Goals
- Full coverage
- Full distribution
- Low area cost
- Fast adaptation
Maze-Routing
- Finding the path
- Detecting disconnected nodes
Results
- Area
- Throughput
- Reconfiguration overhead

## Slide 19: Simulation Methodology
NOCulator[1]
  8x8 mesh for performance analysis
  Synthetic traffic for performance evaluation
  SPEC CPU2006 benchmarks are also evaluated
Maze-Routing[2] implanted in minBD[3] routers
  Deflection-based: deadlock freedom
  Golden and sliver flits: router-level livelock freedom
  Retransmit-once: protocol-level deadlock freedom
[1] NOCulator: https://github.com/CMU-SAFARI/NOCulator
[2] Maze-Routing: https://github.com/CMU-SAFARI/NOCulator/tree/Maze-routing
[3] MinBD: Fallin, Chris, et al. "MinBD: Minimally-buffered deflection routing for energy-efficient interconnect." NoCS 2012.

## Slide 20: Configurations
Maze-Routing
  16 buffer spaces per (minBD) router
Base-line router
  Wormhole buffered routers
  1 VC per port
  40 buffer spaces per router
Faults:
  Links disabled randomly
  From 1 to 5 link failures

## Slide 21: Workloads
Synthetic traffic
  Uniform random traffic with variant injection rates
SPEC CPU2006 benchmarks
  Grouped based on L1 misses per kilo instruction (MPKI)
  3 groups: High (>50), Low (<5), and Medium (rest) intensity
  4 mixes: L (all Low), ML (Medium/Low), M (all Medium), and H (all High).

## Slide 22: Area Overhead
STMicro 60nm technology node
Maze-routing:
  5 copies of alg., 1 per port
ARIADNE:
  Smallest table
  Reconfiguration logic is not implemented
  5 read ports
LBDRe:
  Logic-based method
  Central approach
  Limited coverage
Chart: area (µm2)
| Maze-routing | ARIADNE | LBDRe
8x8 | 1184 | 4471 | 568
16x16 | 1505 | 23921 | 606
3.8 x
2.1 x
27%
15.9 x

## Slide 23: Throughput: Uniform Random Traffic
1 disabled link
5 disabled links
Chart: Injection rate (flits/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.26100000000000001
Maze-routing | 16.3656 | 16.3901 | 16.427 | 16.4865 | 16.5436 | 16.6026 | 16.6973 | 16.793 | 16.935 | 17.1184 | 17.3777 | 17.8938 | 20.5 | 21
up*/down* | 16.1904 | 16.2458 | 16.3292 | 16.4056 | 16.512 | 16.6508 | 16.8173 | 17.0462 | 17.3815 | 17.9013 | 18.8447 | 20.7 | 21
Chart: Injection rate (flits/node/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.26100000000000001
1fail, Maze-routing | 16.3656 | 16.3901 | 16.427 | 16.4865 | 16.5436 | 16.6026 | 16.6973 | 16.793 | 16.935 | 17.1184 | 17.3777 | 17.8938 | 20.5 | 21
Maze-routing | 17.0437 | 17.0828 | 17.1286 | 17.1959 | 17.2697 | 17.3726 | 17.493 | 17.6409 | 17.8588 | 18.215 | 19.3435 | 21
up*/down* | 16.4915 | 16.5727 | 16.6943 | 16.8424 | 17.0816 | 17.5752 | 18.8609 | 21
50%
Sub-optimal paths
Provided path divergence

## Slide 24: Throughput: SPEC CPU
workload mix | Up*/Down* |  | Maze-routing | 
 | 5 failures | no failure | 5 failures | no failure
L | 16.7 | 16.4 | 17.8 | 16.4
ML | 18.8 | 18.2 | 18.9 | 17.2
M | 27.7 | 25.7 | 21.6 | 19.2
H | 54.4 | 50.5 | 25.8 | 23.1
AVG | 29.4 | 27.7 | 21 | 19
Average packet latency
30% latency reduction in average case

## Slide 25: Reconfiguration Overhead
Chart: Time (×104 cycle)
0.2 flits/node/cycle
40K Cycles
66K Cycles
Maze-Routing has no reconfiguration phase

## Slide 26: Summary
A practical fault-tolerant routing algorithm must
  Provide full coverage with guaranteed delivery
  Operate in fully-distributed manner
  Impose low area overhead
  Have low reconfiguration overhead
Maze-Routing is the first work to meet all the above goals
NOCulator and Maze-Routing are available on GitHub
  https://github.com/CMU-SAFARI/NOCulator
  https://github.com/CMU-SAFARI/NOCulator/tree/Maze-routing

## Slide 27: A Low-Overhead, Fully-Distributed, Guaranteed-Delivery Routing Algorithm for Faulty Network-on-Chips
Mohammad Fattah1, Antti Airola1, Rachata Ausavarungnirun2, Nima Mirzaei3, Pasi Liljeberg1, Juha Plosila1, Siamak Mohammadi3, Tapio Pahikkala1, Onur Mutlu2 and Hannu Tenhunen1

## Slide 28: Backup slides

## Slide 29: Area Overhead
Header fields can be coded in 14/17 bits in 8x8/16x16 meshes.
Assuming a baseline router with 144-bit channel width, we need to widen the channel by 10%/12%.
Results in almost 20%/25% increase in the router area.

## Slide 30: Deflection Implications
When a packet is deflected
  Header values are not valid anymore
We need to reset the header values:
  Mode  Normal
  MDbest  MD (next router, dst)
5
4
3
2
4
3
2
1
3
1
4
3
2
1
dst
src
3│

## Slide 31: Delivery Proof
Property: Given there is a path between src and dst, starting from src, by traversing the face underlying line(src,dst), the packet will definitely intersect the line at some point (p) other than src
The MD(p,dst) is definitely smaller than MD(src,dst).
In traversal mode: If MDcur, dst = MDbest with productive output?
  Return to (and act as in) normal mode
 we definitely exit to normal mode
5
4
3
2
4
3
2
1
3
1
4
3
2
1
dst
src

## Slide 32: A Low-Overhead, Fully-Distributed, Guaranteed-Delivery Routing Algorithm for Faulty Network-on-Chips
Mohammad Fattah1, Antti Airola1, Rachata Ausavarungnirun2, Nima Mirzaei3, Pasi Liljeberg1, Juha Plosila1, Siamak Mohammadi3, Tapio Pahikkala1, Onur Mutlu2 and Hannu Tenhunen1