## Slide 1: Revisiting Memory Errors in Large-Scale Production Data Centers Analysis and Modeling of New Trends from the Field
      Justin Meza
Qiang Wu
Sanjeev Kumar
Onur Mutlu

## Slide 2
Overview
Study of DRAM reliability:
on modern devices and workloads
at a large scale in the field

## Slide 3
New reliability trends
Page offlining at scale
Error/failure occurrence
Technology scaling
Modeling errors
Architecture & workload
Overview

## Slide 4
New reliability trends
Page offlining at scale
Technology scaling
Modeling errors
Architecture & workload
Error/failure occurrence
Overview
Errors follow a power-law distribution and a large number of errors occur due to sockets/channels
Notes: Unlike popularly believed, memory errors are not isolated events and can bombard a server, creating a kind of denial of service attack.

## Slide 5
New reliability trends
Page offlining at scale
Modeling errors
Architecture & workload
Error/failure occurrence
Technology scaling
Overview
We find that newer cell fabrication technologies have higher failure rates

## Slide 6
New reliability trends
Page offlining at scale
Modeling errors
Error/failure occurrence
Technology scaling
Architecture & workload
Overview
Chips per DIMM, transfer width, and workload type (not necessarily CPU/memory utilization) affect reliability

## Slide 7
New reliability trends
Page offlining at scale
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors
Overview
We have made publicly available a statistical model for assessing server memory reliability

## Slide 8
New reliability trends
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors
Page offlining at scale
Overview
First large-scale study of page offlining; real-world limitations of technique

## Slide 9
background and motivation
server memory organization
error collection/analysis methodology
memory reliability trends
summary
Outline

## Slide 10
Background and
motivation

## Slide 11
examined extensively in prior work
    charged particles, wear-out
    variable retention time (next talk)
error correcting codes
    used to detect and correct errors
    require additional storage overheads
DRAM errors are common

## Slide 12
Our goal
Strengthen understanding of DRAM reliability by studying:
new trends in DRAM errors
    modern devices and workloads
at a large scale
    billions of device-days, across 14 months

## Slide 13
Our main contributions
identified new DRAM failure trends
developed a model for DRAM errors
evaluated page offlining at scale

## Slide 14
Server memory organization

## Slide 16
Socket

## Slide 17
Memory channels

## Slide 18
DIMM slots

## Slide 19
DIMM

## Slide 20
Chip

## Slide 21
Banks

## Slide 22
Rows and columns

## Slide 23
Cell

## Slide 24
User data
ECC metadata
additional 12.5% overhead

## Slide 25
Reliability events
Fault
the underlying cause of an error
    DRAM cell unreliably stores charge
Error
the manifestation of a fault
permanent: every time
transient: only some of the time

## Slide 26
Error collection/ analysis methodology

## Slide 27
DRAM error measurement
measured every correctable error
    across Facebook's fleet
    for 14 months
    metadata associated with each error
parallelized Map-Reduce to process
used R for further analysis

## Slide 28
System characteristics
6 different system configurations
    Web, Hadoop, Ingest, Database, Cache, Media
    diverse CPU/memory/storage requirements
modern DRAM devices
    DDR3 communication protocol
        (more aggressive clock frequencies)
    diverse organizations (banks, ranks, ...)
    previously unexamined characteristics
        density, # of chips, transfer width, workload

## Slide 29
Memory reliability trends

## Slide 30
New reliability trends
Page offlining at scale
Technology scaling
Modeling errors
Architecture & workload
Error/failure occurrence

## Slide 31
New reliability trends
Page offlining at scale
Technology scaling
Modeling errors
Architecture & workload
Error/failure occurrence

## Slide 32
Server error rate
3%
0.03%
Notes: - Correctable errors occur relatively commonly and affect around 2% of servers each month.

## Slide 33
Memory error distribution

## Slide 34
Memory error distribution
Decreasing hazard rate

## Slide 35
Memory error distribution
Decreasing hazard rate
How are errors mapped to memory organization?

## Slide 36
Sockets/channels: many errors

## Slide 37
Sockets/channels: many errors
Not mentioned in prior chip-level studies

## Slide 38
Sockets/channels: many errors
Not accounted for in prior chip-level studies
At what rate do components fail on servers?

## Slide 39
Bank/cell/spurious failures are common

## Slide 40
# of servers
Denial-of-service–like behavior
# of errors

## Slide 41
# of servers
Denial-of-service–like behavior
# of errors
What factors contribute to memory failures at scale?

## Slide 42
Analytical methodology
measure server characteristics
    not feasible to examine every server
    examined all servers with errors (error group)
    sampled servers without errors (control group)
bucket devices based on characteristics
measure relative failure rate
    of error group vs. control group
    within each bucket

## Slide 43
New reliability trends
Page offlining at scale
Modeling errors
Architecture & workload
Error/failure occurrence
Technology scaling

## Slide 44
inconclusive trends
Prior work found
with respect to memory capacity

## Slide 45
inconclusive trends
Prior work found
with respect to memory capacity
Examine characteristic more closely related to cell fabrication technology

## Slide 46
Use
DRAM chip density
to examine technology scaling
(closely related to fabrication technology)

## Slide 48
Intuition: quadratic increase in capacity

## Slide 49
New reliability trends
Page offlining at scale
Modeling errors
Architecture & workload
Error/failure occurrence
Technology scaling
We find that newer cell fabrication technologies have higher failure rates

## Slide 50
New reliability trends
Page offlining at scale
Modeling errors
Error/failure occurrence
Technology scaling
Architecture & workload

## Slide 51
DIMM architecture
chips per DIMM, transfer width
    8 to 48 chips
    x4, x8 = 4 or 8 bits per cycle
electrical implications

## Slide 52
DIMM architecture
chips per DIMM, transfer width
    8 to 48 chips
    x4, x8 = 4 or 8 bits per cycle
electrical implications
Does DIMM organization affect memory reliability?

## Slide 55
No consistent trend across only chips per DIMM

## Slide 59
More chips ➔ higher failure rate

## Slide 61
More bits per cycle ➔ higher failure rate

## Slide 62
Intuition: increased electrical loading

## Slide 63
Workload dependence
prior studies: homogeneous workloads
    web search and scientific
warehouse-scale data centers:
    web, hadoop, ingest, database, cache, media

## Slide 64
Workload dependence
prior studies: homogeneous workloads
    web search and scientific
warehouse-scale data centers:
    web, hadoop, ingest, database, cache, media
What affect to heterogeneous workloads have on reliability?

## Slide 66
No consistent trend across CPU/memory utilization

## Slide 68
Varies by up to 6.5x

## Slide 69
New reliability trends
Page offlining at scale
Modeling errors
Error/failure occurrence
Technology scaling
Architecture & workload
Chips per DIMM, transfer width, and workload type (not necessarily CPU/memory utilization) affect reliability

## Slide 70
New reliability trends
Page offlining at scale
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors

## Slide 71
A model for server failure
use statistical regression model
    compare control group vs. error group
    linear regression in R
    trained using data from analysis
enable exploratory analysis
    high perf. vs. low power systems

## Slide 72
Memory error
model
Density
Chips
Age
Relative server failure rate
...

## Slide 73
Memory error
model
Density
Chips
Age
Relative server failure rate
...

## Slide 74
Available online
http://www.ece.cmu.edu/~safari/tools/memerr/

## Slide 75
New reliability trends
Page offlining at scale
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors
We have made publicly available a statistical model for assessing server memory reliability

## Slide 76
New reliability trends
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors
Page offlining at scale

## Slide 77
Prior page offlining work
[Tang+,DSN'06] proposed technique
    "retire" faulty pages using OS
    do not allow software to allocate them
[Hwang+,ASPLOS'12] simulated eval.
    error traces from Google and IBM
    recommended retirement on first error
        large number of cell/spurious errors

## Slide 78
Prior page off lining work
[Tang+,DSN'06] proposed technique
    "retire" faulty pages using OS
    do not allow software to allocate them
[Hwang+,ASPLOS'12] simulated eval.
    error traces from Google and IBM
    recommended retirement on first error
        large number of cell/spurious errors
How effective is page offlining in the wild?

## Slide 79
Cluster of 12,276 servers

## Slide 80
-67%
Cluster of 12,276 servers

## Slide 81
-67%
Prior work: -86% to -94%
Cluster of 12,276 servers

## Slide 82
Cluster of 12,276 servers
-67%
Prior work: -86% to -94%
6% of page offlining attempts failed due to OS

## Slide 83
New reliability trends
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors
Page offlining at scale
First large-scale study of page offlining; real-world limitations of technique

## Slide 84
New reliability trends
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors
Page offlining at scale

## Slide 85
Vendors
Age
Processor cores
Correlation analysis
Memory model case study
More results in paper

## Slide 86
Summary

## Slide 87
Modern systems
Large scale

## Slide 88
New reliability trends
Page offlining at scale
Error/failure occurrence
Technology scaling
Modeling errors
Architecture & workload
Summary

## Slide 89
New reliability trends
Page offlining at scale
Technology scaling
Modeling errors
Architecture & workload
Error/failure occurrence
Summary
Errors follow a power-law distribution and a large number of errors occur due to sockets/channels
Notes: Unlike popularly believed, memory errors are not isolated events and can bombard a server, creating a kind of denial of service attack.

## Slide 90
New reliability trends
Page offlining at scale
Modeling errors
Architecture & workload
Error/failure occurrence
Technology scaling
Summary
We find that newer cell fabrication technologies have higher failure rates

## Slide 91
New reliability trends
Page offlining at scale
Modeling errors
Error/failure occurrence
Technology scaling
Architecture & workload
Summary
Chips per DIMM, transfer width, and workload type (not necessarily CPU/memory utilization) affect reliability

## Slide 92
New reliability trends
Page offlining at scale
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors
Summary
We have made publicly available a statistical model for assessing server memory reliability

## Slide 93
New reliability trends
Error/failure occurrence
Technology scaling
Architecture & workload
Modeling errors
Page offlining at scale
Summary
First large-scale study of page offlining; real-world limitations of technique

## Slide 94: Revisiting Memory Errors in Large-Scale Production Data Centers Analysis and Modeling of New Trends from the Field
      Justin Meza
Qiang Wu
Sanjeev Kumar
Onur Mutlu

## Slide 95
Backup slides

## Slide 96
Decreasing hazard rate

## Slide 98
Errors | 54,326 | 0 | 2 | 10
Density | 4Gb | 1Gb | 2Gb | 2Gb

## Slide 99
Density
Errors
Errors | 54,326 | 0 | 2 | 10
Density | 4Gb | 1Gb | 2Gb | 2Gb

## Slide 100
Buckets
Errors
Density
Errors | 54,326 | 0 | 2 | 10
Density | 4Gb | 1Gb | 2Gb | 2Gb

## Slide 101
Errors | 54,326 | 0 | 2 | 10
Density | 4Gb | 1Gb | 2Gb | 2Gb
Errors
Density

## Slide 102
Density
Errors
Errors | 54,326 | 0 | 2 | 10
Density | 4Gb | 1Gb | 2Gb | 2Gb

## Slide 103
Case study

## Slide 104
Output
Inputs
Case study

## Slide 105
Output
Inputs
Case study
Does CPUs or density have a higher impact?

## Slide 106
Exploratory analysis

## Slide 107
Exploratory analysis