## Slide 1: A Heterogeneous Multiple Network-On-Chip Design: An Application-Aware Approach
Asit K. Mishra
Chita R. Das
Onur Mutlu
Notes: Enter Title of Presentation Here
Google Confidential
1

## Slide 2: Executive summary
Problem: Current day NoC designs are agnostic to application requirements and are provisioned for the general case or worst case. Applications have widely differing demands from the network
Our goal: To design a NoC that can satisfy the diverse dynamic performance requirements of applications
Observation: Applications can be divided into two general classes in terms of their requirements from the network: bandwidth-sensitive and latency-sensitive
- Not all applications are equally sensitive to bandwidth and latency
Key idea: Design two NoC
- Each sub-network customized for either BW or LAT sensitive applications
- Propose metrics to classify applications as BW or LAT sensitive
- Prioritize applications’ packets within the sub-networks based on their sensitivity
Network design: BW optimized network has wider link width but operates at a lower frequency and LAT optimized network has narrow link width but operates at a higher frequency
Results: Our proposal is significantly better when compared to an iso-resource monolithic network (5%/3% weighted/instruction throughput improvement and 31% energy reduction)

## Slide 3: Resource requirements of various applications - I
Channel bandwidth affects network latency, throughput and energy/power
Increase in channel BW leads to
  - Reduction in packet serialization
  - Increase in router power
Impact of channel bandwidth on application performance

## Slide 4: Resource requirements of various applications - I
Impact of channel bandwidth on application performance
Simulation settings:
8x8 multi-hop packet based mesh network
Each node in the network has an OoO processor (2GHz), private L1 cache and a router (2GHz)
Shared 1MB per core shared L2
6VC/PC, 2 stage router

## Slide 5: Resource requirements of various applications - I
Impact of channel bandwidth on application performance
Chart: IT (norm. to 64b links)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
64b links | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
128b links | 1.0074 | 1.0889 | 1.0052 | 1.0233 | 1.1096 | 1.1208 | 1.1171 | 1.1533 | 1.2822 | 1.2167 | 1.4184 | 1.5092 | 1.3037 | 1.4722 | 1.4728 | 1.6504 | 1.3879 | 1.4368 | 1.7701 | 1.7085 | 1.9357 | 1.6242 | 1.8895 | 1.9987 | 2.0467 | 1.8539 | 2.1157 | 1.9603 | 2.2238 | 2.0095
256b links | 1.0107 | 1.1104 | 1.0076 | 1.0353 | 1.148 | 1.1723 | 1.1709 | 1.2177 | 1.3989 | 1.268 | 1.5308 | 1.6483 | 1.3692 | 1.7602 | 1.6773 | 1.8547 | 1.4678 | 1.6001 | 2.2035 | 2.3153 | 2.9201 | 2.0442 | 2.4729 | 3.1896 | 3.2964 | 2.696 | 2.9843 | 3.686 | 3.5513 | 3.8871
512b links | 1.0118 | 1.1121 | 1.0085 | 1.0792 | 1.1684 | 1.2007 | 1.188 | 1.227 | 1.3969 | 1.2898 | 1.5603 | 1.7079 | 1.4078 | 1.8401 | 1.7562 | 1.9131 | 1.5482 | 1.6597 | 2.3428 | 2.4737 | 3.0915 | 2.1209 | 2.5662 | 3.9123 | 3.65 | 2.867 | 3.1221 | 5.2843 | 5.4657 | 6.6688

## Slide 6: Resource requirements of various applications - I
Impact of channel bandwidth on application performance
Chart: IT (norm. to 64b links)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
64b links | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
128b links | 1.0074 | 1.0889 | 1.0052 | 1.0233 | 1.1096 | 1.1208 | 1.1171 | 1.1533 | 1.2822 | 1.2167 | 1.4184 | 1.5092 | 1.3037 | 1.4722 | 1.4728 | 1.6504 | 1.3879 | 1.4368 | 1.7701 | 1.7085 | 1.9357 | 1.6242 | 1.8895 | 1.9987 | 2.0467 | 1.8539 | 2.1157 | 1.9603 | 2.2238 | 2.0095
256b links | 1.0107 | 1.1104 | 1.0076 | 1.0353 | 1.148 | 1.1723 | 1.1709 | 1.2177 | 1.3989 | 1.268 | 1.5308 | 1.6483 | 1.3692 | 1.7602 | 1.6773 | 1.8547 | 1.4678 | 1.6001 | 2.2035 | 2.3153 | 2.9201 | 2.0442 | 2.4729 | 3.1896 | 3.2964 | 2.696 | 2.9843 | 3.686 | 3.5513 | 3.8871
512b links | 1.0118 | 1.1121 | 1.0085 | 1.0792 | 1.1684 | 1.2007 | 1.188 | 1.227 | 1.3969 | 1.2898 | 1.5603 | 1.7079 | 1.4078 | 1.8401 | 1.7562 | 1.9131 | 1.5482 | 1.6597 | 2.3428 | 2.4737 | 3.0915 | 2.1209 | 2.5662 | 3.9123 | 3.65 | 2.867 | 3.1221 | 5.2843 | 5.4657 | 6.6688
18/30 (21/36 total) applications’ performance is agnostic to channel BW (8x BW inc. → less than 2x performance inc.)

## Slide 7: Resource requirements of various applications - I
Impact of channel bandwidth on application performance
Chart: IT (norm. to 64b links)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
64b links | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
128b links | 1.0074 | 1.0889 | 1.0052 | 1.0233 | 1.1096 | 1.1208 | 1.1171 | 1.1533 | 1.2822 | 1.2167 | 1.4184 | 1.5092 | 1.3037 | 1.4722 | 1.4728 | 1.6504 | 1.3879 | 1.4368 | 1.7701 | 1.7085 | 1.9357 | 1.6242 | 1.8895 | 1.9987 | 2.0467 | 1.8539 | 2.1157 | 1.9603 | 2.2238 | 2.0095
256b links | 1.0107 | 1.1104 | 1.0076 | 1.0353 | 1.148 | 1.1723 | 1.1709 | 1.2177 | 1.3989 | 1.268 | 1.5308 | 1.6483 | 1.3692 | 1.7602 | 1.6773 | 1.8547 | 1.4678 | 1.6001 | 2.2035 | 2.3153 | 2.9201 | 2.0442 | 2.4729 | 3.1896 | 3.2964 | 2.696 | 2.9843 | 3.686 | 3.5513 | 3.8871
512b links | 1.0118 | 1.1121 | 1.0085 | 1.0792 | 1.1684 | 1.2007 | 1.188 | 1.227 | 1.3969 | 1.2898 | 1.5603 | 1.7079 | 1.4078 | 1.8401 | 1.7562 | 1.9131 | 1.5482 | 1.6597 | 2.3428 | 2.4737 | 3.0915 | 2.1209 | 2.5662 | 3.9123 | 3.65 | 2.867 | 3.1221 | 5.2843 | 5.4657 | 6.6688
18/30 (21/36 total) applications’ performance is agnostic to channel BW (8x BW inc. → less than 2x performance inc.)
2. 12/30 (15/36 total) applications’ performance scale with increase in channel BW (8x BW inc. → at least 2x performance inc.)

## Slide 8: Resource requirements of various applications - II
Reduction in router latency (by increasing frequency)
  Reduction in packet latency
  Increase in router power consumption
Impact of network latency on application performance

## Slide 9: Resource requirements of various applications - II
Simulation settings:
… same as last experiment
128b links
Added dummy stages (2-cycle and 4-cycle ) to each router
Impact of network latency on application performance

## Slide 10: Resource requirements of various applications - II
Chart: IT (norm. to 2-cycle router)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
2-cycle router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
4-cycle router | 0.90155 | 0.94414 | 0.90155 | 0.90155 | 0.90155 | 0.94414 | 0.95011 | 0.93496 | 0.92433 | 0.95153 | 0.94948 | 0.92928 | 0.9391 | 0.9391 | 0.93486 | 0.95554 | 0.96199 | 0.93416 | 0.98524 | 0.99745 | 0.98556 | 0.98548 | 0.9945 | 0.98231 | 0.98534 | 0.98315 | 0.99332 | 0.99169 | 0.98094 | 0.98604
6-cycle router | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.83784 | 0.82139 | 0.7 | 0.82604 | 0.82604 | 0.72 | 0.74 | 0.71 | 0.72 | 0.78 | 0.77 | 0.72 | 0.84 | 0.9163 | 0.94796 | 0.89524 | 0.90017 | 0.9235 | 0.92602 | 0.91733 | 0.90473 | 0.95753 | 0.92962 | 0.95524
Impact of network latency on application performance

## Slide 11: Resource requirements of various applications - II
Chart: IT (norm. to 2-cycle router)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
2-cycle router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
4-cycle router | 0.90155 | 0.94414 | 0.90155 | 0.90155 | 0.90155 | 0.94414 | 0.95011 | 0.93496 | 0.92433 | 0.95153 | 0.94948 | 0.92928 | 0.9391 | 0.9391 | 0.93486 | 0.95554 | 0.96199 | 0.93416 | 0.98524 | 0.99745 | 0.98556 | 0.98548 | 0.9945 | 0.98231 | 0.98534 | 0.98315 | 0.99332 | 0.99169 | 0.98094 | 0.98604
6-cycle router | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.83784 | 0.82139 | 0.7 | 0.82604 | 0.82604 | 0.72 | 0.74 | 0.71 | 0.72 | 0.78 | 0.77 | 0.72 | 0.84 | 0.9163 | 0.94796 | 0.89524 | 0.90017 | 0.9235 | 0.92602 | 0.91733 | 0.90473 | 0.95753 | 0.92962 | 0.95524
18/30 (21/36 total) applications’ performance is sensitive to network latency (3x latency reduction → at least 25% performance improvement)
Impact of network latency on application performance

## Slide 12: Resource requirements of various applications - II
Chart: IT (norm. to 2-cycle router)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
2-cycle router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
4-cycle router | 0.90155 | 0.94414 | 0.90155 | 0.90155 | 0.90155 | 0.94414 | 0.95011 | 0.93496 | 0.92433 | 0.95153 | 0.94948 | 0.92928 | 0.9391 | 0.9391 | 0.93486 | 0.95554 | 0.96199 | 0.93416 | 0.98524 | 0.99745 | 0.98556 | 0.98548 | 0.9945 | 0.98231 | 0.98534 | 0.98315 | 0.99332 | 0.99169 | 0.98094 | 0.98604
6-cycle router | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.83784 | 0.82139 | 0.7 | 0.82604 | 0.82604 | 0.72 | 0.74 | 0.71 | 0.72 | 0.78 | 0.77 | 0.72 | 0.84 | 0.9163 | 0.94796 | 0.89524 | 0.90017 | 0.9235 | 0.92602 | 0.91733 | 0.90473 | 0.95753 | 0.92962 | 0.95524
2. 12/30 (15/36 total) applications’ performance is marginally sensitive to network latency (3x latency increase → less than 15% performance improvement)
18/30 (21/36 total) applications’ performance is sensitive to network latency (3x latency reduction → at least 25% performance improvement)
Impact of network latency on application performance

## Slide 13: Application-aware approach to designing multiple NoCs
Chart: IT (norm. to 2-cycle router)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
2-cycle router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
4-cycle router | 0.90155 | 0.94414 | 0.90155 | 0.90155 | 0.90155 | 0.94414 | 0.95011 | 0.93496 | 0.92433 | 0.95153 | 0.94948 | 0.92928 | 0.9391 | 0.9391 | 0.93486 | 0.95554 | 0.96199 | 0.93416 | 0.98524 | 0.99745 | 0.98556 | 0.98548 | 0.9945 | 0.98231 | 0.98534 | 0.98315 | 0.99332 | 0.99169 | 0.98094 | 0.98604
6-cycle router | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.83784 | 0.82139 | 0.7 | 0.82604 | 0.82604 | 0.72 | 0.74 | 0.71 | 0.72 | 0.78 | 0.77 | 0.72 | 0.84 | 0.9163 | 0.94796 | 0.89524 | 0.90017 | 0.9235 | 0.92602 | 0.91733 | 0.90473 | 0.95753 | 0.92962 | 0.95524
Chart: IT (norm. to 64b links)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
64b links | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
128b links | 1.0074 | 1.0889 | 1.0052 | 1.0233 | 1.1096 | 1.1208 | 1.1171 | 1.1533 | 1.2822 | 1.2167 | 1.4184 | 1.5092 | 1.3037 | 1.4722 | 1.4728 | 1.6504 | 1.3879 | 1.4368 | 1.7701 | 1.7085 | 1.9357 | 1.6242 | 1.8895 | 1.9987 | 2.0467 | 1.8539 | 2.1157 | 1.9603 | 2.2238 | 2.0095
256b links | 1.0107 | 1.1104 | 1.0076 | 1.0353 | 1.148 | 1.1723 | 1.1709 | 1.2177 | 1.3989 | 1.268 | 1.5308 | 1.6483 | 1.3692 | 1.7602 | 1.6773 | 1.8547 | 1.4678 | 1.6001 | 2.2035 | 2.3153 | 2.9201 | 2.0442 | 2.4729 | 3.1896 | 3.2964 | 2.696 | 2.9843 | 3.686 | 3.5513 | 3.8871
512b links | 1.0118 | 1.1121 | 1.0085 | 1.0792 | 1.1684 | 1.2007 | 1.188 | 1.227 | 1.3969 | 1.2898 | 1.5603 | 1.7079 | 1.4078 | 1.8401 | 1.7562 | 1.9131 | 1.5482 | 1.6597 | 2.3428 | 2.4737 | 3.0915 | 2.1209 | 2.5662 | 3.9123 | 3.65 | 2.867 | 3.1221 | 5.2843 | 5.4657 | 6.6688

## Slide 14: Application-aware approach to designing multiple NoCs
Chart: IT (norm. to 2-cycle router)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
2-cycle router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
4-cycle router | 0.90155 | 0.94414 | 0.90155 | 0.90155 | 0.90155 | 0.94414 | 0.95011 | 0.93496 | 0.92433 | 0.95153 | 0.94948 | 0.92928 | 0.9391 | 0.9391 | 0.93486 | 0.95554 | 0.96199 | 0.93416 | 0.98524 | 0.99745 | 0.98556 | 0.98548 | 0.9945 | 0.98231 | 0.98534 | 0.98315 | 0.99332 | 0.99169 | 0.98094 | 0.98604
6-cycle router | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.83784 | 0.82139 | 0.7 | 0.82604 | 0.82604 | 0.72 | 0.74 | 0.71 | 0.72 | 0.78 | 0.77 | 0.72 | 0.84 | 0.9163 | 0.94796 | 0.89524 | 0.90017 | 0.9235 | 0.92602 | 0.91733 | 0.90473 | 0.95753 | 0.92962 | 0.95524
Based on the observations:
Applications can be classified into distinct classes: typically LAT/BW sensitive
LAT sensitive applications can benefit from low network latency
BW sensitive applications can benefit from high network bandwidth
Not all applications are equally sensitive to either LAT or BW
Monolithic network cannot optimize both classes simultaneously
Chart: IT (norm. to 64b links)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
64b links | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
128b links | 1.0074 | 1.0889 | 1.0052 | 1.0233 | 1.1096 | 1.1208 | 1.1171 | 1.1533 | 1.2822 | 1.2167 | 1.4184 | 1.5092 | 1.3037 | 1.4722 | 1.4728 | 1.6504 | 1.3879 | 1.4368 | 1.7701 | 1.7085 | 1.9357 | 1.6242 | 1.8895 | 1.9987 | 2.0467 | 1.8539 | 2.1157 | 1.9603 | 2.2238 | 2.0095
256b links | 1.0107 | 1.1104 | 1.0076 | 1.0353 | 1.148 | 1.1723 | 1.1709 | 1.2177 | 1.3989 | 1.268 | 1.5308 | 1.6483 | 1.3692 | 1.7602 | 1.6773 | 1.8547 | 1.4678 | 1.6001 | 2.2035 | 2.3153 | 2.9201 | 2.0442 | 2.4729 | 3.1896 | 3.2964 | 2.696 | 2.9843 | 3.686 | 3.5513 | 3.8871
512b links | 1.0118 | 1.1121 | 1.0085 | 1.0792 | 1.1684 | 1.2007 | 1.188 | 1.227 | 1.3969 | 1.2898 | 1.5603 | 1.7079 | 1.4078 | 1.8401 | 1.7562 | 1.9131 | 1.5482 | 1.6597 | 2.3428 | 2.4737 | 3.0915 | 2.1209 | 2.5662 | 3.9123 | 3.65 | 2.867 | 3.1221 | 5.2843 | 5.4657 | 6.6688

## Slide 15: Application-aware approach to designing multiple NoCs
Chart: IT (norm. to 2-cycle router)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
2-cycle router | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
4-cycle router | 0.90155 | 0.94414 | 0.90155 | 0.90155 | 0.90155 | 0.94414 | 0.95011 | 0.93496 | 0.92433 | 0.95153 | 0.94948 | 0.92928 | 0.9391 | 0.9391 | 0.93486 | 0.95554 | 0.96199 | 0.93416 | 0.98524 | 0.99745 | 0.98556 | 0.98548 | 0.9945 | 0.98231 | 0.98534 | 0.98315 | 0.99332 | 0.99169 | 0.98094 | 0.98604
6-cycle router | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.80601 | 0.83784 | 0.82139 | 0.7 | 0.82604 | 0.82604 | 0.72 | 0.74 | 0.71 | 0.72 | 0.78 | 0.77 | 0.72 | 0.84 | 0.9163 | 0.94796 | 0.89524 | 0.90017 | 0.9235 | 0.92602 | 0.91733 | 0.90473 | 0.95753 | 0.92962 | 0.95524
Solution
Two NoCs where each (sub)network is optimized for either LAT or BW sensitive applications
Chart: IT (norm. to 64b links)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
64b links | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
128b links | 1.0074 | 1.0889 | 1.0052 | 1.0233 | 1.1096 | 1.1208 | 1.1171 | 1.1533 | 1.2822 | 1.2167 | 1.4184 | 1.5092 | 1.3037 | 1.4722 | 1.4728 | 1.6504 | 1.3879 | 1.4368 | 1.7701 | 1.7085 | 1.9357 | 1.6242 | 1.8895 | 1.9987 | 2.0467 | 1.8539 | 2.1157 | 1.9603 | 2.2238 | 2.0095
256b links | 1.0107 | 1.1104 | 1.0076 | 1.0353 | 1.148 | 1.1723 | 1.1709 | 1.2177 | 1.3989 | 1.268 | 1.5308 | 1.6483 | 1.3692 | 1.7602 | 1.6773 | 1.8547 | 1.4678 | 1.6001 | 2.2035 | 2.3153 | 2.9201 | 2.0442 | 2.4729 | 3.1896 | 3.2964 | 2.696 | 2.9843 | 3.686 | 3.5513 | 3.8871
512b links | 1.0118 | 1.1121 | 1.0085 | 1.0792 | 1.1684 | 1.2007 | 1.188 | 1.227 | 1.3969 | 1.2898 | 1.5603 | 1.7079 | 1.4078 | 1.8401 | 1.7562 | 1.9131 | 1.5482 | 1.6597 | 2.3428 | 2.4737 | 3.0915 | 2.1209 | 2.5662 | 3.9123 | 3.65 | 2.867 | 3.1221 | 5.2843 | 5.4657 | 6.6688

## Slide 16: Design methodology
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor

## Slide 17: Design methodology
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor
1
Identify LAT/BW sensitive applications
- Proposes a novel dynamic application classification scheme
1

## Slide 18: Design methodology
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor
1
Identify LAT/BW sensitive applications
- Proposes a novel dynamic application classification scheme
1
2
Design sub-networks based on applications’ demand
- This network architecture is better than a monolithic iso-resource network
2

## Slide 19: Design methodology
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor
1
Identify LAT/BW sensitive applications
- Proposes a novel dynamic application classification scheme
1
2
Design sub-networks based on applications’ demand
- This network architecture is better than a monolithic iso-resource network
2
DEMUX

## Slide 20: Design: Dynamic classification of applications
Network episode
Compute episode
time
Application life cycle
Outstanding network packets

## Slide 21: Design: Dynamic classification of applications
Network episode
Compute episode
time
Application life cycle
App. has at least one outstanding packet
Processor is likely stalling → low IPC
Outstanding network packets

## Slide 22: Design: Dynamic classification of applications
Network episode
Compute episode
time
Application life cycle
App. has at least one outstanding packet
Processor is likely stalling → low IPC
App. has no outstanding packet
High IPC
Outstanding network packets

## Slide 23: Design: Dynamic classification of applications
Network episode
Compute episode
Episode height
Episode length
time
Application life cycle
App. has at least one outstanding packet
Processor is likely stalling → low IPC
App. has no outstanding packet
High IPC
Episode length = Number of consecutive cycles there are net. packets
Episode height = Avg. number of L1 packets injected during an episode
Outstanding network packets
Notes: Length is the number of cycles the episode lasts starting from when the first packet is injected into the network until there are no more outstanding packets belonging to that episode.
Height is the average number of packets (L1 misses) injected by the application during the network episode.

## Slide 24: Design: Dynamic classification of applications
Network episode
Compute episode
time
Application life cycle
App. has at least one outstanding packet
Processor is likely stalling → low IPC
App. has no outstanding packet
High IPC
Outstanding network packets
Short episode ht.: Low MLP, each request is critical (LAT sensitive)
Tall episode ht.: High MLP (BW sensitive)
Short episode len.: Packets are very critical (LAT sensitive)
Long episode len.: Latency tolerant (could be de-prioritized)
Episode length
Episode height

## Slide 25: Classification and ranking
Classification |  |  | Length | 
 |  | Long | Medium | Short
 | Tall | gems, mcf | sphinx, lbm, cactus, xalan | sjeng, tonto
Height | Medium | omnetpp, apsi | ocean, sjbb, sap, bzip, sjas, soplex, tpc | applu, perl, barnes, gromacs, namd, calculix, gcc, povray, h264, gobmk, hmmer, astar
 | Short | leslie | art, libq, milc, swim | wrf, deal
Classification: LAT/BW

## Slide 26: Classification and ranking
Classification: LAT/BW
Ranking |  |  | Length | 
 |  | Long | Medium | Short
 | High | Rank-4 | Rank-2 | Rank-1
Height | Medium | Rank-3 | Rank-2 | Rank-2
 | Short | Rank-4 | Rank-3 | Rank-1
Ranking: Sensitivity to LAT/BW
Classification |  |  | Length | 
 |  | Long | Medium | Short
 | Tall | gems, mcf | sphinx, lbm, cactus, xalan | sjeng, tonto
Height | Medium | omnetpp, apsi | ocean, sjbb, sap, bzip, sjas, soplex, tpc | applu, perl, barnes, gromacs, namd, calculix, gcc, povray, h264, gobmk, hmmer, astar
 | Short | leslie | art, libq, milc, swim | wrf, deal

## Slide 27: Network design
1N-128

## Slide 28: Network design
1N-128
2N-64x256-ST
(Steering)

## Slide 29: Network design
1N-128
2N-64x256-ST
(Steering)
2N-64x256-ST-RK
(Steering+Ranking)

## Slide 30: Network design
1N-128
2N-64x256-ST
(Steering)
2N-64x256-ST-RK
(Steering+Ranking)
2N-64x256-ST-RK(FS)
(Steering+Ranking and Frequency Scaling)

## Slide 31: Network design
1N-128
1N-256
2N-64x256-ST
(Steering)
2N-64x256-ST-RK
(Steering+Ranking)
2N-64x256-ST-RK(FS)
(Steering+Ranking and Frequency Scaling)
1N-512 (High BW)
2N-128X128
1N-320
(iso-BW)
1N-320(FS)
(iso-resource)

## Slide 32: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)

## Slide 33: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)

## Slide 34: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
+18%
Performance (25 WL with 50% BW and 50% LAT)

## Slide 35: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)
+7%
+18%

## Slide 36: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)
+5%
+7%
+18%

## Slide 37: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)
5%
+5%
+7%
+18%

## Slide 38: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)
w. 2%
5%
+5%
+7%
+18%

## Slide 39: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)
w. 2%
w. 2%
5%
+5%
+7%
+18%

## Slide 40: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)
w. 2%
w. 2%
5%
+5%
+7%
+18%
Chart: Normalized energy
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
Energy | 1 | 1.38 | 1.02 | 1.75 | 1.42 | 1.33 | 1.16 | 1.49 | 1.63
Energy (25 WL with 50% BW and 50% LAT)
47%
59%

## Slide 41: Analysis
Chart: Weighted speedup
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
WS | 38.88 | 44.14 | 43.98 | 53.15 | 46.02 | 48.79 | 52.18 | 49.84 | 53.18
Performance (25 WL with 50% BW and 50% LAT)
w. 2%
w. 2%
5%
+5%
+7%
+18%
Chart: Normalized energy
| 1N-128 | 1N-256 | 2N-128x128 | 1N-512 | 2N-64x256-ST | 2N-64x256-ST+RK(no FS) | 2N-64x256-ST+RK(FS) | 1N-320(no FS) | 1N-320 (FS)
Energy | 1 | 1.38 | 1.02 | 1.75 | 1.42 | 1.33 | 1.16 | 1.49 | 1.63
Energy (25 WL with 50% BW and 50% LAT)
47%
59%
Best EDP across all designs

## Slide 42: Conclusions
Problem: Current day NoC designs are agnostic to application requirements and are provisioned for the general case or worst case. Applications have widely differing demands from the network
Our goal: To design a NoC that can satisfy the diverse dynamic performance requirements of applications
Observation: Applications can be divided into two general classes in terms of their requirements from the network: bandwidth-sensitive and latency-sensitive
- Not all applications are equally sensitive to bandwidth and latency
Key idea: Design two NoC
- Each sub-network customized for either BW or LAT sensitive applications
- Propose metrics to classify applications as BW or LAT sensitive
- Prioritize applications’ packets within the sub-networks based on their sensitivity
Network design: BW optimized network has wider link width but operates at a lower frequency and LAT optimized network has narrow link width but operates at a higher frequency
Results: Our proposal is significantly better when compared to an iso-resource monolithic network (5%/3% weighted/instruction throughput improvement and 31% energy reduction)

## Slide 43: Thank you
Q?
Asit Mishra
asit.k.mishra@intel.com

## Slide 44: Backup Slides . . .

## Slide 45: Other metrics considered for application classification
Chart: L1/L2 MPKI
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
L1MPKI | 0.1 | 0.55 | 2.66 | 3.15 | 3.31 | 3.84 | 5.15 | 6.41 | 6.62 | 8.5 | 10.33 | 12.24 | 12.32 | 15.91 | 16.85 | 18.8 | 22.73 | 22.03 | 24.02 | 25.04 | 25.03 | 28.9 | 28.9 | 37.16 | 40.29 | 46.71 | 53.4 | 57.42 | 106.72 | 120.23
L2MPKI | 0.05 | 0.46 | 0.4 | 1.28 | 1.79 | 0.63 | 4.24 | 3.4 | 2.79 | 6.44 | 7.35 | 1.65 | 12.09 | 6.43 | 3.9 | 18.47 | 2.95 | 8.93 | 6.76 | 3.59 | 23.32 | 15 | 11.48 | 18.45 | 6.11 | 37.04 | 19.58 | 55.47 | 69.9 | 102.15
Slack | 24.46 | 41.4844 | 38.665 | 27.9688 | 51.6875 | 58.375 | 68.9375 | 97.9688 | 117.953 | 117.656 | 124.406 | 95.3125 | 189.5 | 175.484 | 107.641 | 320.25 | 104.938 | 262.33 | 157.938 | 151.938 | 364.016 | 316.094 | 214.359 | 338.172 | 227.562 | 742.812 | 226.062 | 442.734 | 761.141 | 1823.45

## Slide 46: Analysis of network episode length and height
Chart: Avg. episode height (network packets)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
Avg. Episode Height | 6.817 | 1.7814 | 1.0636 | 1.2686 | 9.3106 | 2.9548 | 3.005 | 3.1315 | 3.8511 | 4.826 | 4.2507 | 7.8198 | 1.917 | 5.3053 | 2.7973 | 2.4508 | 4.9221 | 1.9282 | 2.5983 | 6.3953 | 10.8225 | 8.6508 | 3.118 | 9.2336 | 4.7759 | 4.663 | 12.2385 | 6.398 | 10.8347 | 12.0313
Chart: Avg. episode length (in cycles)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
Avg. Episode Length | 374.3954 | 463.4529 | 11776.3352 | 359.4547 | 261.6161 | 150.4538 | 364.236 | 353.433 | 366.8438 | 524.8792 | 551.88 | 263.6629 | 5378.3545 | 613.8798 | 564.3671 | 2755.202 | 500.7455 | 1973.5588 | 807.1797 | 809.3317 | 903.7175 | 914.6877 | 1675.9189 | 929.3259 | 1460.7568 | 4665.0229 | 1522.2482 | 18085.9162 | 336454.9763 | 457949.8607
Short length/height
Medium length/height
Long length/High height
0.3M
10K
0.4M
18K

## Slide 47: Analysis of network episode length and height
Chart: Avg. episode height (network packets)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
Avg. Episode Height | 6.817 | 1.7814 | 1.0636 | 1.2686 | 9.3106 | 2.9548 | 3.005 | 3.1315 | 3.8511 | 4.826 | 4.2507 | 7.8198 | 1.917 | 5.3053 | 2.7973 | 2.4508 | 4.9221 | 1.9282 | 2.5983 | 6.3953 | 10.8225 | 8.6508 | 3.118 | 9.2336 | 4.7759 | 4.663 | 12.2385 | 6.398 | 10.8347 | 12.0313
Chart: Avg. episode length (in cycles)
| applu | wrf | art | deal | sjeng | barnes | grmcs | namd | h264 | gcc | pvray | tonto | libq | gobmk | astar | milc | hmmer | swim | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf
Avg. Episode Length | 374.3954 | 463.4529 | 11776.3352 | 359.4547 | 261.6161 | 150.4538 | 364.236 | 353.433 | 366.8438 | 524.8792 | 551.88 | 263.6629 | 5378.3545 | 613.8798 | 564.3671 | 2755.202 | 500.7455 | 1973.5588 | 807.1797 | 809.3317 | 903.7175 | 914.6877 | 1675.9189 | 929.3259 | 1460.7568 | 4665.0229 | 1522.2482 | 18085.9162 | 336454.9763 | 457949.8607
Short length/height
Medium length/height
Long length/High height
Based on performance scaling sensitivity to bandwidth and frequency
0.3M
10K
0.4M
18K

## Slide 48: Empirical results to support the classification
SPECjbb (sjbb) as cut-off for BW/LAT sensitive applications

## Slide 49: Empirical results to support the classification
SPECjbb (sjbb) as cut-off for BW/LAT sensitive applications

## Slide 50: Empirical results to support the classification
SPECjbb (sjbb) as cut-off for BW/LAT sensitive applications

## Slide 51: Empirical results to support the classification
SPECjbb (sjbb) as cut-off for BW/LAT sensitive applications

## Slide 52: Empirical results to support the classification
SPECjbb (sjbb) as cut-off for BW/LAT sensitive applications
Why 9 clusters?
Chart: Number of clusters
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0
 | 210 | 112.9272 | 54.3281 | 41.7993 | 35.6336 | 25.1291 | 23.8931 | 16.6199 | 15.9997 | 15.0431 | 11.3501 | 10.5141 | 11.311 | 9.3088 | 9.0505 | 5.8818 | 8.7167 | 7.326 | 6.8244 | 4.9773 | 2.7337 | 5.4971 | 4.0175 | 4.8952 | 2.8246 | 1.2434 | 4.4123 | 0.68382 | 4.4361 | 3.4497 | 0.62833 | 0.38268 | 0.4818 | 0.47044 | 0.37095 | 0.23

## Slide 53: Empirical results to support the classification
SPECjbb (sjbb) as cut-off for BW/LAT sensitive applications
Why 9 clusters?
Chart: Number of clusters
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0
 | 210 | 112.9272 | 54.3281 | 41.7993 | 35.6336 | 25.1291 | 23.8931 | 16.6199 | 15.9997 | 15.0431 | 11.3501 | 10.5141 | 11.311 | 9.3088 | 9.0505 | 5.8818 | 8.7167 | 7.326 | 6.8244 | 4.9773 | 2.7337 | 5.4971 | 4.0175 | 4.8952 | 2.8246 | 1.2434 | 4.4123 | 0.68382 | 4.4361 | 3.4497 | 0.62833 | 0.38268 | 0.4818 | 0.47044 | 0.37095 | 0.23
13x

## Slide 54: Empirical results to support the classification
SPECjbb (sjbb) as cut-off for BW/LAT sensitive applications
Why 9 clusters?
Chart: Number of clusters
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0
 | 210 | 112.9272 | 54.3281 | 41.7993 | 35.6336 | 25.1291 | 23.8931 | 16.6199 | 15.9997 | 15.0431 | 11.3501 | 10.5141 | 11.311 | 9.3088 | 9.0505 | 5.8818 | 8.7167 | 7.326 | 6.8244 | 4.9773 | 2.7337 | 5.4971 | 4.0175 | 4.8952 | 2.8246 | 1.2434 | 4.4123 | 0.68382 | 4.4361 | 3.4497 | 0.62833 | 0.38268 | 0.4818 | 0.47044 | 0.37095 | 0.23

## Slide 55: Analysis with varying workload combinations
Chart: WS and IT (norm. to 1N-128 net.)
| 0% BANDWIDTH 100% LATENCY | 25% BANDWIDTH 75% LATENCY | 50% BANDWIDTH 50% LATENCY | 75% BANDWIDTH 25% LATENCY | 100% BANDWIDTH 0% LATENCY
WS | 1.0381 | 1.2732 | 1.3421 | 1.3938 | 1.27
IT | 1.0859 | 1.2171 | 1.2428 | 1.2072 | 1.4725

## Slide 56: Comparison to prior works
Chart: WS and IT (norm. to 1N-128 net.)
| 1N-128-STC | 1N-128-ST+RK | 2N-128x128-LD-BAL | 2N-64x256-W-LD-BAL | 2N-64x256-ST+RK(FS)
WS | 1.0568 | 1.1116 | 1.1312 | 1.1597 | 1.3421
IT | 1.0334 | 1.0831 | 1.1069 | 1.1425 | 1.2428

## Slide 57: Dynamic steering of packets
Chart: % packets in sub-network
| applu | wrf | art | deal | barnes | grmcs | namd | h264 | gcc | pvray | libq | gobmk | astar | milc | hmmer | swim | leslie | perl | calculix | tonto | sjeng | sjbb | sap | xalan | sphnx | bzip | lbm | sjas | soplx | cacts | omnet | gems | mcf | apsi | ocean | tpc
Bandwidth-optimized network | 3 | 2 | 2 | 5 | 4 | 2 | 4 | 6 | 2 | 4 | 8 | 4 | 2 | 5 | 6 | 8 | 18 | 4 | 4 | 82 | 81 | 85 | 88 | 88 | 90 | 88 | 93 | 94 | 92 | 96 | 98 | 99 | 99 | 96 | 97 | 94
Latency-optimized network | 97 | 98 | 98 | 95 | 96 | 98 | 96 | 94 | 98 | 96 | 92 | 96 | 98 | 95 | 94 | 92 | 82 | 96 | 96 | 18 | 19 | 15 | 12 | 12 | 10 | 12 | 7 | 6 | 8 | 4 | 2 | 1 | 1 | 4 | 3 | 6

## Slide 58: Design: Putting it all together
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor
MUX

## Slide 59: Design: Putting it all together
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor
MUX
Classify applications based on sensitivity to network BW/LAT

## Slide 60: Design: Putting it all together
Episode LEN/HT
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor
MUX
Classify applications based on sensitivity to network BW/LAT
Use network episode length/height to dynamically identify apps

## Slide 61: Design: Putting it all together
Episode LEN/HT
Design LAT/BW optimized networks
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor
MUX
Classify applications based on sensitivity to network BW/LAT
Use network episode length/height to dynamically identify apps

## Slide 62: Design: Putting it all together
Classify applications based on sensitivity to network BW/LAT
Episode LEN/HT
Design LAT/BW optimized networks
Processors/L1$
Network
L2$ and Mem. Controllers
Logical view of a multicore processor
MUX
Use network episode length/height to dynamically identify apps
Prioritization within networks

## Slide 63: Summary
A NoC paradigm based on top-down approach (application demand/requirement analysis)
An efficient design paradigm for future heterogeneous multicores

## Slide 64: Summary
A NoC paradigm based on top-down approach (application demand/requirement analysis)
An efficient design paradigm for future heterogeneous multicores
Small core
GPGPUs
Accelerators/ ASIC
Latency critical
Throughput (BW) critical
Throughput (BW) critical
Latency critical (real-time constraints)
Big core

## Slide 65: Summary
A NoC paradigm based on top-down approach (application demand/requirement analysis)
An efficient design paradigm for future heterogeneous multicores
Small core
GPGPUs
Accelerators/ ASIC
Latency critical
Big core
Providing all these guarantees in one network is hard
Multiple networks: each customized for one metric
Throughput (BW) critical
Throughput (BW) critical
Latency critical (real-time constraints)

## Slide 66: Summary
A NoC paradigm based on top-down approach (application demand/requirement analysis)
An efficient design paradigm for future heterogeneous multicore m/c
Latency
Throughput
Local communication
Long haul comm.
Power
1 cycle/ bufferless/Faster routers
1 cycle/ high bandwidth
Power efficient links/DVFS router
Hybrid/ fewer connectivity network
Butterfly/express channels
MUX
Share 2D space or 3D layers
Episode LEN/HT/??