## Slide 1
Jawad Haj-Yahya
Yanos Sazeides2 Mohammed Alser1 Efraim Rotem3 Onur Mutlu1
Techniques for Reducing
the Connected-Standby Energy Consumption
of Mobile Devices
1
2
1
3
1
Notes: Thanks for the introduction.
Good morning everyone. I’m Jawad and today I’m presenting our work about Techniques for Reducing the Connected-Standby Energy Consumption of Mobile Devices.
This work was mainly done at Intel, in collaboration with SAFARI research group from ETH Zurich and the university of Cyprus.
[END]

## Slide 2: Executive Summary
Motivation: Mobile devices operate in connected-standby mode most of the time. We would like to make this mode more energy efficient.
Problem: In connected-standby mode, mobile devices enter the Deepest-Runtime-Idle-Power State (DRIPS). There are three sources of energy inefficiency in modern DRIPS:
  Wake-up timer event is toggled in a high-leakage process using a high frequency clock.
  Several IO signals are always powered on.
  Processor context is preserved in high-leakage-power SRAMs.
Goal: Reduce power consumption of DRIPS.
Mechanism: Optimized DRIPS (ODRIPS) based on they key ideas:
  Offload wake-up timer to a low leakage chip (e.g., chipset) with significantly slower clock.
  Offload always-on IO functionality to power-gate all processor IOs.
  Transfer processor context to a secure memory region inside DRAM.
Evaluation:
  We implement ODRIPS in Intel's Skylake mobile processor.
  ODRIPS reduces the platform average power consumption in connected-standby mode by 22%.
Notes: First, I’ll give a high level overview of the talk.
…
[END]

## Slide 3: Presentation Outline
Connected-Standby and DRIPS Overview
The ODRIPS Substrate
  Wake-up timer event handling
  Offload processor’s always-on IO functionality
  Transfers the processor context to DRAM
Evaluation
Summary
Notes: First let me give you a background on connected-standby and DRIPS
[END]

## Slide 4: Connected-Standby Mode (1)
Mobile devices (phones, tablets, and laptops) are idle the majority (~90%) of the time.
During idle periods, modern mobile devices
  Operate at low-power state to increase battery life
  Remain connected to a communication network for usability (e.g., for email notifications and phone calls).
This operation mode is called connected-standby
  Microsoft's Modern Standby
  Apple's Power Nap
In the connected-standby mode
  The system spends most of its time in the Deepest-Runtime-Idle-Power-State (DRIPS)
  Display panel is off during connected-standby
SoC
Z Z Z
Notes: So what exactly is connected –standby?
[READ TEXT]
[END]

## Slide 5: Connected-Standby Mode (2)
~0.5% of the time (3W)
 ~20% of the average power
~99.5% of the time ( ~60mW )
 ~80% of the average power
~100ms
Periodic Interval
Periodic Interval
~30sec
~80% of the connected-standby platform average power is consumed in DRIPS
Notes: In connected-standby mode, the system operates in a periodic interval
In each interval there is an Active and Idle states
In Active part the OS kernel performs maintains functions
Most of the time the system is Idle and enters DRIPS
According to our estimates, the transition from Active to Idle state takes 200us
And the transition from Idle state to Active state takes about 300us
On average the Active residency is 0.5% and consumes 3W
The idle residency is 99.5% and consumes 60mW
[READ]
[END]

## Slide 6: DRIPS: Deepest Runtime Idle Power State
Three major power consumption sources in DRIPS :
Processor
Chipset
24MHz XTAL
AON IOs
CKE
SA Save/
Restore SRAM
Cores/GFX Save/Restore SRAM
DRAM
32KHz XTAL
VCC AON
Wake-up Timer
PMU
Chipset-PMU
1) Wake-up timer event is toggled in a high-leakage process using a high frequency clock (5% of the platform average power ).
2) Several IO signals are always powered-on (7% of the platform average power ).
3) Processor context is preserved in high-leakage power SRAMs (9% of the platform average power ).
15% of the platform
average power
We target these three inefficiencies
Chipset includes relatively slow IO (e.g., USB/SATA/PCI) and system power management functions.
The chipset process is optimized for low-leakage and low-frequencies.
The processor operates in high frequencies (e.g., 3GHz).
The processor process is optimized for high frequency rather than low-leakage
Intel Skylake Mobile Architecture
Notes: In the figure we see a processors and it’s chipset
A chipset is a chip that includes several slow IO such as USB/SATA/PCI/Audio and system power management functions
Chipset is fabricated with process that is optimized for low-leakage
The processor is optimized for high frequency rather than low-leakage
[READ] DRIPS has three ….
[READ] Wake-up timer …
Wake-up timer is used for waking up the processor after a time determined by OS or PMU
[READ] Several IO signals …
IO that supplies clock, communication between the processor and other components
[READ] Processor context …
The context is used to restore the state of processor components when exiting DRIPS

## Slide 7: Presentation Outline
Connected-Standby and DRIPS Overview
The ODRIPS Substrate
  Wake-up timer event handling
  Offload processor’s always-on IO functionality
  Transfers the processor context to DRAM
Evaluation
Summary
Notes: Now I will explain how we tackle these three inefficiencies
[END]

## Slide 8: ODRIPS: Optimized DRIPS
ODRIPS consists of three key ideas
Processor
Chipset
24MHz XTAL
AON IOs
CKE
SA Save/
Restore SRAM
Cores/GFX Save/Restore SRAM
DRAM
32KHz XTAL
VCC AON
Wake-up Timer
PMU
Chipset-PMU
Idea 1. Offload wake-up timer to a low leakage chip (e.g., chipset) and significantly slower clock (5% of the platform average power ).
Idea 2. Offload always-on IO functionality to chipset and power-gate all processor IOs (7% of the platform average power).
Idea 3. Transfer processor context to a
secure memory region inside DRAM (9% of the platform average power).
15% (idea in the paper)
Notes: ODRIPS consists of three key idea …
First idea …
Second idea …
Third idea …
[CLICK]
We have and idea to tackle the DRAM self-refresh

## Slide 9: Presentation Outline
Connected-Standby and DRIPS Overview
The ODRIPS Substrate
  Wake-up timer event handling
  Offload processor’s always-on IO functionality
  Transfers the processor context to DRAM
Evaluation
Summary
Notes: Now I will explain how we tackle the first problem
[END]

## Slide 10: Idea 1: Wake-up Timer Handling
Problem 1: Wake-up timer event handling consumes 5% of platform power in DRIPS.
Key idea 1: Offload wake-up timer to a low-leakage chip (e.g., chipset) and significantly slower clock.
Notes: [READ] ..
[END]

## Slide 11: Idea 1: Wake-up Timer Handling
24MHz XTAL
DRAM
32KHz XTAL
Timer
PMU
Chipset-PMU
Fast Timer
1
Slow Timer
Step
Step = 24MHz/32KHz
(in fixed-point)
Calibration is required
Processor
Chipset
ODRIPS Architecture
Baseline Architecture
Notes: In the baseline architecture, the timer is toggled using 24MHz inside the processor's PMU
This is done in a high-leakage process and using a relatively high clock frequency (24MHz)
We offload the timer to the chipset which is fabricated with low leakage process and we use the 32KHz to toggle the timer
For this purpose, we add 2 timers to the chipset: fast-timer that is toggled with the 24MHz increments by 1
And the 2nd timer is a slow-timer which increments by a step. Step is the ratio between the clocks,
Step is represented as a fixed-point and is calibrated once every boot
[END]

## Slide 12: Idea 1: Wake-up Timer Handling
Processor
Chipset
24MHz XTAL
DRAM
32KHz XTAL
Timer
PMU
Chipset-PMU
Fast Timer
1
Slow Timer
Step
Active
Idle
Runtime
This idea saves 5% of the DRIPS power
Notes: When the system moves from Active to Idle,
First we transfer the timer from the processor to the fast-timer in the chipset and turn-off the processor’s timer
Then the system transfer the fast-timer into the slow-timer
At this stage we turn-off the fast-timer and the 24MHz crystal clock
This idea saves 5% of the platform average power

## Slide 13: Presentation Outline
Connected-Standby and DRIPS Overview
The ODRIPS Substrate
  Wake-up timer event handling
  Offload processor’s always-on IO functionality
  Transfers the processor context to DRAM
Evaluation
Summary
Notes: Now, I will describe the 2nd idea

## Slide 14: Idea 2: Offload Always-On IOs
Problem 2: Several IO signals are always-on in DRIPS consuming 7% of platform average power.
Key idea 2: Offload the always-on IO signals functionality to chipset and dynamically power-gate these IOs.
Notes: [READ]

## Slide 15: Baseline Always-On IOs
Processor
Chipset
24MHz XTAL
AON IOs
DRAM
32KHz XTAL
VCC AON
PMU
Chipset-PMU
EC
Thermal reporting
24MHz clock
Power management links
Debug (JTAG)
Always-On IOs:
Debug
Notes: Two new component appear in the figure
EC is an embedded controller that does multiple functionalities including system thermal management, and
Debug component that connects to the JTAGs of both processor and chipset
The IO signals that are always-on in the baseline architecture are … [READ]
[END]

## Slide 16: Idea 2: Offload Always-On IOs
Processor
Chipset
24MHz XTAL
AON IOs
DRAM
32KHz XTAL
VCC AON
Chipset-PMU
24MHz clock is no longer needed after offloading the timer to chipset
No need for power management in ODRIPS
Offload the Embedded Controller (EC) thermal reporting to chipset using General Purpose IO (GPIO)
Debug is not required in ODRIPS – use chipset debug
EC
PMU
Debug
Thermal reporting
24MHz clock
Power management links
Debug (JTAG)
This idea saves 7% of the DRIPS power
Notes: Let’s see how we can get rid of these signals in ODRIPS and power-gate them
[READ]
[END]

## Slide 17: Presentation Outline
Connected-Standby and DRIPS Overview
The ODRIPS Substrate
  Wake-up timer event handling
  Offload processor’s always-on IO functionality off-chip
  Transfers the processor context to DRAM
Evaluation
Summary
Notes: Now I will explain about the 3rd idea

## Slide 18: Idea 3: Transfers Processor Context to DRAM
Problem 3: Leakage power consumption of the Save/Restore SRAMs that saves the processor context is high and consuming 9% of the platform average power in DRIPS.
Key idea 3: Dynamically transfer the processor context from the SRAMs to DRAM.
Notes: [READ]

## Slide 19: Idea 3: Transfers Processor Context to DRAM
Processor
Chipset
SA Save/
Restore SRAM
Cores/GFX Save/Restore SRAM
DRAM
VCC AON
PMU
Chipset-PMU
Non Protected
DRAM
SGX Protected Memory
Processor Context
We move the processor context from save/restore SRAMs to SGX protected Memory
A 200KB out of the 128MB of SGX memory is “stolen” to save the processor context
This idea saves 9% of the DRIPS power
Notes: [READ]
Two FSMs are implemented in order to flush the processor context from SRAMs into DRAM
The DRAM preserves all its content via self-refresh mode including the processors context

## Slide 20: Presentation Outline
Connected-Standby and DRIPS Overview
The ODRIPS Substrate
  Wake-up timer event handling
  Offload processor’s always-on IO functionality off-chip
  Transfers the processor context to DRAM
Evaluation
Summary
Notes: Now, I will move on to the evaluation.

## Slide 21: Methodology
Intel Skylake for mobile devices includes ODRIPS.
We evaluate ODRIPS using a real Intel Skylake system.
We used Keysight measurement instruments
We use an in-house power model for sensitivity studies.
Notes: [READ]
[READ]
The figure in the left illustrates the Keysight measurement instrument connected to our design under test (DUT) - one channel is shown
The Figure on the right shows the measurement setting in our lab. A DUT connected to the to the Keysight measurement instruments and the laptop collects the measurement data
[END]

## Slide 22: Results
Chart: Platform Average Power [%]
| Baseline | Wake-up timer offloading | Wake-up offloading & AON IO gating | Move context to DRAM | ODRIPS
Others | 0.31451 | 0.31451 | 0.31451 | 0.31451 | 0.31461
DRAM Self-Refresh | 0.11437 | 0.11437 | 0.11437 | 0.11437 | 0.11437
Power Delivery | 0.21434 | 0.19853 | 0.17912 | 0.1902 | 0.15502
24MHz crystal | 0.03574 | 0 | 0 | 0.03574 | 0
Save/Restore SRAMs | 0.068048 | 0.068334 | 0.068048 | 0.00014296 | 0.00014296
AON IOs | 0.054324 | 0.054324 | 0 | 0.054324 | 0
Wake-up&Timer | 0.0090064 | 0 | 0 | 0.0090064 | 0
DRAM CKE | 0.0070049 | 0.0070049 | 0.0070049 | 0.0070049 | 0.0070049
Active&Transitions | 0.18267 | 0.18305 | 0.18343 | 0.18319 | 0.18449
Platfrom AvgP | 1 | 0.94012 | 0.86648 | 0.90848 | 0.77563
22%
ODRIPS reduces the connected-standby platform average power by 22%
Notes: Let me start with showing the platform average power benefits of each one of the three ideas compared to baseline showing in first column
The first ideas shows 6% platform average power reduction in connected standby
The second idea combined with the first idea shows 13% average power reduction
Then the third idea shows 9% average power reduction
All the three ideas combined shows 22% average power reduction
[READ]
[END]

## Slide 23: Other Results in the Paper
Using Non-Volatile Memories (NVMs) with ODRIPS
  An idea to use Phase Change Memory (PCM) instead of DRAM
    This idea reduces connected-standby platform average power by additional 15%.
  Use embedded MRAM (eMRAM) instead of on-chip SRAMs
Connected-standby platform average power sensitivity to:
  Core frequency in Active state
  DRAM frequency in Active state
Notes: Other results are available in the paper
[READ] Use NVM …
We also have a bunch of sensitivity studies for core and DRAM frequencies in active state …
[END]

## Slide 24: Presentation Outline
Connected-Standby and DRIPS Overview
The ODRIPS Substrate
  Wake-up timer event handling
  Offload processor’s always-on IO functionality off-chip
  Transfers the processor context to DRAM
Evaluation
Summary
Notes: Let me quickly show the summary of my talk now.

## Slide 25: Summary
Motivation: Mobile devices operate in connected-standby mode most of the time. We would like to make this mode more energy efficient.
Problem: In connected-standby mode, mobile devices enter the Deepest-Runtime-Idle-Power State (DRIPS). There are three sources of energy inefficiency in modern DRIPS:
  Wake-up timer event is toggled in a high-leakage process using a high frequency clock.
  Several IO signals are always powered on.
  Processor context is preserved in high-leakage-power SRAMs.
Goal: Reduce power consumption of DRIPS.
Mechanism: Optimized DRIPS (ODRIPS) based on they key ideas:
  Offload wake-up timer to a low leakage chip (e.g., chipset) with significantly slower clock.
  Offload always-on IO functionality to power-gate all processor IOs.
  Transfer processor context to a secure memory region inside DRAM.
Evaluation:
  We implement ODRIPS in Intel's Skylake mobile processor.
  ODRIPS reduces the platform average power consumption in connected-standby mode by 22%.
Notes: [READ]

## Slide 26
Jawad Haj-Yahya
Yanos Sazeides2 Mohammed Alser1 Efraim Rotem3 Onur Mutlu1
Techniques for Reducing
the Connected-Standby Energy Consumption
of Mobile Devices
1
2
1
3
1
Notes: Thank you for your attention!
I will be happy to take any question.
[END]

## Slide 27: Backup

## Slide 28: Results – Use NVMe
Chart: Platform Average Power [%]
| Baseline | ODRIPS | ODRIPS with eMRAM | ODRIPS with PCM
Others | 0.31451 | 0.31461 | 0.31461 | 0.31461
DRAM Self-Refresh | 0.11437 | 0.11437 | 0.11437 | 0
Power Delivery | 0.21434 | 0.15502 | 0.15502 | 0.11188
24MHz crystal | 0.03574 | 0 | 0 | 0
Save/Restore SRAMs | 0.068048 | 0.00014296 | 0.00014296 | 0.00014296
AON IOs | 0.054324 | 0 | 0 | 0
Wake-up&Timer | 0.0090064 | 0 | 0 | 0
DRAM CKE | 0.0070049 | 0.0070049 | 0.0070049 | 0
Active&Transitions | 0.18267 | 0.18449 | 0.18443 | 0.20401
Platfrom AvgP | 1 | 0.77563 | 0.775 | 0.63064
15%

## Slide 29: Results – Core and DRAM Freq.
Chart: Platform Average Power [%]
| Baseline | ODRIPS | ODRIPS with eMRAM | ODRIPS with PCM
Others | 0.31451 | 0.31461 | 0.31461 | 0.31461
DRAM Self-Refresh | 0.11437 | 0.11437 | 0.11437 | 0
Power Delivery | 0.21434 | 0.15502 | 0.15502 | 0.11188
24MHz crystal | 0.03574 | 0 | 0 | 0
Save/Restore SRAMs | 0.068048 | 0.00014296 | 0.00014296 | 0.00014296
AON IOs | 0.054324 | 0 | 0 | 0
Wake-up&Timer | 0.0090064 | 0 | 0 | 0
DRAM CKE | 0.0070049 | 0.0070049 | 0.0070049 | 0
Active&Transitions | 0.18267 | 0.18449 | 0.18443 | 0.20401
Platfrom AvgP | 1 | 0.77563 | 0.775 | 0.63064
DRAM Frequencies
Core Frequencies

## Slide 30
Processor
Chipset
24MHz XTAL
AON IOs
CKE
SA Save/
Restore SRAM
Cores/GFX Save/Restore SRAM
DRAM
32KHz XTAL
VCC AON
Wake-up Timer
PMU
Chipset-PMU
Chart: 
| Chipset | Panel | DRAM Self-Refresh | Storage | Communication | Power Delivery | Rest of platform | 24MHz crystal (XTAL) | SA Save/Restore SRAMs | Cores/GFX Save/Restore SRAMs | Wake-up (AON) IO | Wake-up &timer (inside PMU) | DRAM CKE
 | 3.5 | 0 | 8 | 3 | 4 | 15 | 11.5 | 2.5 | 1.66 | 3.12 | 3.8 | 0.63 | 0.49
DRIPS: deepest runtime idle power state
List all components

## Slide 31: ODRIPS: Optimized DRIPS
Processor
Chipset
24MHz XTAL
AON IOs
CKE
SA Save/
Restore SRAM
Cores/GFX Save/Restore SRAM
DRAM
32KHz XTAL
VCC AON
Wake-up Timer
PMU
Chipset-PMU
1) Offload wake-up timer to a low leakage chip (e.g., chipset) and significantly slower clock
2) Offload always-on IOs functionality to other chip and power-gate all processor IOs
3) Transfer processor context to a secure memory region inside DRAM