## Slide 1
Mosaic: A GPU Memory Manager
with Application-Transparent Support for Multiple Page Sizes
Rachata Ausavarungnirun, Joshua Landgraf, Vance Miller , Saugata Ghose, Jayneel Gandhi, Christopher J. Rossbach, Onur Mutlu
GPU Core
Private TLB
GPU Core
GPU Core
GPU Core
Shared TLB
Private TLB
Page Table Walkers
Page Table
Private TLB
Private TLB
Limited TLB reach
High latency page walks
Data
CPU Memory
High latency
I/O
Private
Shared
CPU-side
GPU-side
Chart: Number of Concurrently-Executing Applications
4KB (with demand paging overhead) | 0.59944 | 0.45122 | 0.36621 | 0.31252 | 0.17741
2MB (with demand paging overhead) | 0.045119 | 0.0092086 | 0.003699 | 0.00062629 | 0.00035554
How to achieve the best of both page sizes?
Page Size Trade-Off
Design Goals
Exploit benefits of both small and large pages
  High TLB Reach
  Low demand paging overhead
No data movement
Application transparency
  Programmers do not need to modify GPGPU applications
Large Page Frame
Large Page Frame
Coalesced Large Page Frame
State-of-the-Art Memory Allocation
Cannot coalesce
(without moving multiple 4K pages)
Unallocated
App 1
App 2
In-Place Coalescing
Mosaic
Need to search which pages to coalesce
Challenges with Multiple Page Sizes
High overhead
Hardware
Contiguity-Conserving
Allocation
In-Place
Coalescer
Contiguity-Aware
Compaction
Application
Demands Data
GPU Runtime
Allocate Memory
Page
Table
Data
Transfer
Done
List of Large Pages
Coalesce
Pages
System I/O Bus
Transfer Data
Contiguity-Conserving
Allocation
In-Place
Coalescer
Application
Deallocates Data
Page
Table
Data
Splinter
Pages
Contiguity-Aware
Compaction
List of free pages
Data Allocation
Data Deallocation
High-Level Overview of Mosaic
Mosaic Soft Guarantee
A large page frame contains
pages from only a single address space
Results
1
2
3
4
5
6
1
2
3
GPU Support for Virtual Memory
Improves programmability with a unified address space
Enables large data sets to be processed in the GPU
Allows multiple applications to run on a GPU
23.7%
43.1%
31.5%
21.4%
Homogeneous
Heterogeneous
39.0%
33.8%
55.4%
61.5%
95.0%
Chart: Number of Concurrently-Executing Applications
| 1 | 2 | 3 | 4 | 5 | 2 | 3 | 4 | 5
GPU-MMU | 0.518 | 1.4767 | 2.5642 | 4.1118 | 3.8973 | 1.6789 | 2.5839 | 3.6544 | 4.3729
Mosaic | 1.01 | 2.3846 | 3.985 | 5.502 | 5.4158 | 2.0388 | 3.3972 | 5.2309 | 5.4071
Ideal TLB | 1.02 | 2.6669 | 4.3529 | 5.9314 | 5.7774 | 2.409 | 4.4413 | 5.6679 | 6.3187
Chart: Number of Concurrently-Executing Applications
| 1 App | 2 Apps | 3 Apps | 4 Apps | 5 Apps
GPU-MMU | 0.7429 | 0.62639 | 0.70418 | 0.6658 | 0.62973
Mosaic | 0.9983 | 0.9983 | 0.9983 | 0.9983 | 0.9983
 | 1
GPU-MMU | 0.8633 | 0.81619 | 0.77807 | 0.76004 | 0.62871
Mosaic | 0.9983 | 0.9983 | 0.9983 | 0.9983 | 0.9983
Chart: Fragmentation Index
| 0.3 | 0.5 | 0.7 | 0.9 | 0.95 | 0.97 | 1
no CAC | 1 | 1 | 1 | 1 | 1 | 1 | 1
CAC | 1 | 1 | 1 | 1.391 | 1.303 | 1.244 | 1.115
CAC-BC | 1 | 1 | 1 | 1.391 | 1.303 | 1.2455 | 1.13
CAC-Ideal | 1 | 1 | 1 | 1.401 | 1.457 | 1.467 | 1.472
Small Pages:
Low demand paging overhead
Limited TLB reach
Large Pages:
Better TLB reach
High demand paging overhead
Overhead of Address Translation Without Demand Paging
Overhead of Both Address Translation and Demand Paging
CPU
Memory
Apply soft guarantee
Coalescing
0
Coalesced Bit
1
Large Page Table
Small Page Table
Application transparency
Data can be accessed using either page size
No TLB flush
Large Page Frames
Large Page Frames
Free large page
Free large page
Compaction
Compaction
Only triggered when memory is heavily fragmented
Goals
Reduce memory fragmentation
Free up large page frames
Heavily-fragmented GPU memory
Compacted pages has no virtual contiguity
No longer coalesceable
Fully-allocated large page frames  Coalesceable
Methodology
GPGPU-Sim (MAFIA) configured to a GTX 750 Ti
Multiple GPGPU applications can execute concurrently
Model page walks and page tables
Model virtual-to-physical address mapping
Available at: https://github.com/CMU-SAFARI/Mosaic
Chart: Normalized Performance
| BFS2 | BP | GUPS | HISTO | HS | JPEG | LIB | LPS | LUD | MM | RED | SCAN | SCP | TRD | Average
4KB | 0.85721 | 0.86506 | 0.98963 | 0.32367 | 0.52887 | 0.39596 | 0.25917 | 0.49598 | 0.97934 | 0.29811 | 0.57283 | 0.93092 | 0.91073 | 0.49589 | 0.51806
2MB | 1.0103 | 0.98291 | 1 | 0.99668 | 0.97867 | 0.94978 | 0.97277 | 1.0277 | 0.99889 | 0.99938 | 1.015 | 1.0302 | 0.97625 | 0.96168 | 0.99234