## Slide 1: A Case for Efficient Hardware/Software Cooperative Management of Storage and Memory
Justin Meza*, Yixin Luo*, Samira Khan*†, Jishen Zhao§,
Yuan Xie§‡, and Onur Mutlu*
*Carnegie Mellon University
§Pennsylvania State University
†Intel Labs ‡AMD Research

## Slide 2: Overview
Traditional systems have a two-level storage model
  Access volatile data in memory with a load/store interface
  Access persistent data in storage with a file system interface
  Problem: Operating system (OS) and file system (FS) code and buffering for storage lead to energy and performance inefficiencies
Opportunity: New non-volatile memory (NVM) technologies can help provide fast (similar to DRAM), persistent storage (similar to Flash)
  Unfortunately, OS and FS code can easily become energy efficiency and performance bottlenecks if we keep the traditional storage model
This work: makes a case for hardware/software cooperative management of storage and memory within a single-level
  We describe the idea of a Persistent Memory Manager (PMM) for efficiently coordinating storage and memory, and quantify its benefit
  And, examine questions and challenges to address to realize PMM

## Slide 3: Talk Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 4: A Tale of Two Storage Levels
Traditional systems use a two-level storage model
  Volatile data is stored in DRAM
  Persistent data is stored in HDD and Flash
Accessed through two vastly different interfaces
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …

## Slide 5: A Tale of Two Storage Levels
Two-level storage arose in systems due to the widely different access latencies and methods of the commodity storage devices
  Fast, low capacity, volatile DRAM  working storage
  Slow, high capacity, non-volatile hard disk drives  persistent storage
Data from slow storage media is buffered in fast DRAM
  After that it can be manipulated by programs  programs cannot directly access persistent storage
  It is the programmer’s job to translate this data between the two formats of the two-level storage (files and data structures)
Locating, transferring, and translating data and formats between the two levels of storage can waste significant energy and performance

## Slide 6: Opportunity: New Non-Volatile Memories
Emerging memory technologies provide the potential for unifying storage and memory (e.g., Phase-Change, STT-RAM, RRAM)
  Byte-addressable (can be accessed like DRAM)
  Low latency (comparable to DRAM)
  Low power (idle power better than DRAM)
  High capacity (closer to Flash)
  Non-volatile (can enable persistent storage)
  May have limited endurance (but, better than Flash)
Can provide fast access to both volatile data and persistent storage
Question: if such devices are used, is it efficient to keep a two-level storage model?

## Slide 7: Eliminating Traditional Storage Bottlenecks
Today (DRAM + HDD) and two-level storage model
Replace HDD with NVM (PCM-like), keep two-level storage model
Replace HDD and DRAM with NVM (PCM-like), eliminate all OS+FS overhead
Results for PostMark
Notes: On the x axis are three system designs that we will look at throughout this talk.
The system on the left is a traditional HDD Baseline system that uses DRAM for volatile memory and an HDD for storage and all of the levels of operating system and file system code and buffering required to access persistent data.
The system in the middle is an NVM Baseline system that simply replaces the HDD for NVM – and doesn’t change anything else.
The system on the right is equipped with a Persistent Memory composed entirely of NVM. It manages the placement and location of data using hardware and software and does not execute any OS or FS code to access persistent data.
On the y axis is the fraction of total energy consumed by these systems normalized to the HDD baseline and averaged across the workloads we will later evaluate. As we can see, simply switching the HDD for NVM can greatly reduce total system energy consumption, as is expected from future systems employing such technology. But what is less obvious is how much energy can be reduced by switching from the traditional two-level storage model of the NVM Baseline to the single-level storage model of the Persistent Memory. As we can see, the energy savings can be quite drastic: reducing energy by around 80% on average.
Let’s take a look at where these energy savings come from.

## Slide 8: Eliminating Traditional Storage Bottlenecks
Results for PostMark

## Slide 9: Where is Energy Spent in Each Model?
HDD access
wastes energy
FS/OS overhead becomes important
Additional DRAM energy due to buffering overhead of two-level model
No FS/OS overhead
No additional buffering overhead in DRAM
Results for PostMark
Notes: This figure shows the same systems as before, but breaks down how the they consume energy among several different categories:
User CPU – on the bottom – is the amount of energy consumed by the process executing code on the CPU.
Syscall CPU is the amount of energy consumed to execute the operating system and file system on the program’s behalf on the CPU. Notice that the Persistent Memory system does not consume energy in this category because it does away with OS and FS code for persistent data.
DRAM, NVM, and HDD are the amounts of energy consumed to access and operate each of those devices.
What we can see from this graph is that while the energy spent handling persistent data in the traditional HDD Baseline system is dwarfed by the energy of accessing its devices, in the NVM Baseline system – by just switching the HDD with NVM – the energy consumed to manage persistent data in the traditional way begins to emerge as a significant bottleneck. By eliminating this source of inefficiency in the Persistent Memory system, however, we can improve energy (and as we will later see, performance as well).

## Slide 10: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 11: Our Proposal: Coordinated HW/SW Memory and Storage Management
Goal: Unify memory and storage to eliminate wasted work to locate, transfer, and translate data
  Improve both energy and performance
  Simplify programming model as well

## Slide 12: Our Proposal: Coordinated HW/SW Memory and Storage Management
Goal: Unify memory and storage to eliminate wasted work to locate, transfer, and translate data
  Improve both energy and performance
  Simplify programming model as well
Before: Traditional Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …

## Slide 13: Our Proposal: Coordinated HW/SW Memory and Storage Management
Goal: Unify memory and storage to eliminate wasted work to locate, transfer, and translate data
  Improve both energy and performance
  Simplify programming model as well
After: Coordinated HW/SW Management
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback

## Slide 14: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 15: The Persistent Memory Manager
Persistent Memory Manager
  Exposes a load/store interface to access persistent data
  Manages data placement, location, persistence, security
  Manages metadata storage and retrieval
  Exposes hooks and interfaces for system software
Example program manipulating a persistent object:
Create persistent object and its handle
Allocate a persistent array and assign
Load/store interface
Notes: Here is an example of what a program might look like if written for a system equipped with a persistent memory.
The main function creates a new persistent object called “myData” with the handle “file.dat”. You can see that we use a similar notation to C’s FILE structure. The contents of myData is then set to a newly-allocated *persistent* array of 64 integers.
Later (perhaps after reboots of the machine), the data for the handle “file.dat” is retrieved and the contents of myData is modified and will remain persistent.

## Slide 16: Putting Everything Together
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 17: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 18: Opportunities and Benefits
We’ve identified at least five opportunities and benefits of a unified storage/memory system that gets rid of the two-level model:
  Eliminating system calls for file operations
  Eliminating file system operations
  Efficient data mapping/location among heterogeneous devices
  Providing security and reliability in persistent memories
  Hardware/software cooperative data management

## Slide 19: Eliminating System Calls for File Operations
A persistent memory can expose a large, linear, persistent address space
  Persistent storage objects can be directly manipulated with load/store operations
This eliminates the need for layers of operating system code
  Typically used for calls like open, read, and write
Also eliminates OS file metadata
  File descriptors, file buffers, and so on

## Slide 20: Eliminating File System Operations
Locating files is traditionally done using a file system
  Runs code and traverses structures in software to locate files
Existing hardware structures for locating data in virtual memory can be extended and adapted to meet the needs of persistent memories
  Memory Management Units (MMUs), which map virtual addresses to physical addresses
  Translation Lookaside Buffers (TLBs), which cache mappings of virtual-to-physical address translations
Potential to eliminate file system code
At the cost of additional hardware overhead to handle persistent data storage

## Slide 21: Efficient Data Mapping among Heterogeneous Devices
A persistent memory exposes a large, persistent address space
  But it may use many different devices to satisfy this goal
  From fast, low-capacity volatile DRAM to slow, high-capacity non-volatile HDD or Flash
  And other NVM devices in between
Performance and energy can benefit from good placement of data among these devices
  Utilizing the strengths of each device and avoiding their weaknesses, if possible
  For example, consider two important application characteristics: locality and persistence

## Slide 22: Efficient Data Mapping among Heterogeneous Devices
Notes: Here, we’ve plotted these two important characteristics as axes on a graph. On the bottom is persistence, from temporary – the data does not need to be saved across program executions – on the left to persistent – the data must remain across executions for correct operation – on the right. From bottom to top we have data that has more locality – and is accessed very frequently in a short amount of time or space – to data that has less locality – which may predominantly be accessed in a random manner.
Let’s take a look at two examples of data and how they map onto this space.

## Slide 23: Efficient Data Mapping among Heterogeneous Devices
X
Columns in a column store that are scanned through only infrequently
 place on Flash
Notes: First we have some data that requires high persistence but has little locality. Such data might be the columns in a column store that are only scanned through infrequently. While it is essential that this data remain persistent across runs of the program, it may not be accessed that frequently, and therefore may be more beneficial to place on slightly slower, persistent memory devices, such as Flash.

## Slide 24: Efficient Data Mapping among Heterogeneous Devices
X
Columns in a column store that are scanned through only infrequently
 place on Flash
X
Frequently-updated index for a Content Delivery Network (CDN)  place in DRAM
Applications or system software can provide hints for data placement
Notes: On the other end of the perspective is data that has high locality but is only ephemeral and not needed between executions. Data in a Content Delivery Network that is cached as it is accessed and is constantly being updated and replaced, is a great candidate for placing in DRAM on such systems.

## Slide 25: Providing Security and Reliability
A persistent memory deals with data at the granularity of bytes and not necessarily files
  Provides the opportunity for much finer-grained security and protection than traditional two-level storage models provide/afford
  Need efficient techniques to avoid large metadata overheads
A persistent memory can improve application reliability by ensuring updates to persistent data are less vulnerable to failures
  Need to ensure that changes to copies of persistent data placed in volatile memories become persistent

## Slide 26: HW/SW Cooperative Data Management
Persistent memories can expose hooks and interfaces to applications, the OS, and runtimes
  Have the potential to provide improved system robustness and efficiency than by managing persistent data with either software or hardware alone
Can enable fast checkpointing and reboots, improve application reliability by ensuring persistence of data
  How to redesign availability mechanisms to take advantage of these?
Persistent locks and other persistent synchronization constructs can enable more robust programs and systems

## Slide 27: Quantifying Persistent Memory Benefits
We have identified several opportunities and benefits of using persistent memories without the traditional two-level store model
We will next quantify:
  How do persistent memories affect system performance?
  How much energy reduction is possible?
  Can persistent memories achieve these benefits despite additional access latencies to the persistent memory manager?

## Slide 28: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 29: Evaluation Methodology
Hybrid real system / simulation-based approach
  System calls are executed on host machine (functional correctness) and timed to accurately model their latency in the simulator
  Rest of execution is simulated in Multi2Sim (enables hardware-level exploration)
Power evaluated using McPAT and memory power models
16 cores, 4-wide issue, 128-entry instruction window, 1.6 GHz
Volatile memory: 4GB DRAM, 4KB page size, 100-cycle latency
Persistent memory
  HDD (measured): 4ms seek latency, 6Gbps bus rate
  NVM: (modeled after PCM) 4KB page size, 160-/480-cycle (read/write) latency

## Slide 30: Evaluated Systems
HDD Baseline (HB)
  Traditional system with volatile DRAM memory and persistent HDD storage
  Overheads of operating system and file system code and buffering
HDD without OS/FS (HW)
  Same as HDD Baseline, but with the ideal elimination of all OS/FS overheads
  System calls take 0 cycles (but HDD access takes normal latency)
NVM Baseline (NB)
  Same as HDD Baseline, but HDD is replaced with NVM
  Still has OS/FS overheads of the two-level storage model
Persistent Memory (PM)
  Uses only NVM (no DRAM) to ensure full-system persistence
  All data accessed using loads and stores
  Does not waste energy on system calls
  Data is manipulated directly on the NVM device

## Slide 31: Evaluated Workloads
Unix utilities that manipulate files
  cp: copy a large file from one location to another
  cp –r: copy files in a directory tree from one location to another
  grep: search for a string in a large file
  grep –r: search for a string recursively in a directory tree
PostMark: an I/O-intensive benchmark from NetApp
  Emulates typical access patterns for email, news, web commerce
MySQL Server: a popular database management system
  OLTP-style queries generated by Sysbench
  MySQL (simple): single, random read to an entry
  MySQL (complex): reads/writes 1 to 100 entries per transaction

## Slide 32: Performance Results

## Slide 33: Performance Results: HDD w/o OS/FS
For HDD-based systems, eliminating OS/FS overheads typically leads to small performance improvements  execution time dominated by HDD access latency

## Slide 34: Performance Results: HDD w/o OS/FS
Though, for more complex file system operations like directory traversal (seen with cp -r and grep -r), eliminating the OS/FS overhead improves performance

## Slide 35: Performance Results: HDD to NVM
Switching from an HDD to NVM greatly reduces execution time due to NVM’s much faster access latencies, especially for I/O-intensive workloads (cp, PostMark, MySQL)

## Slide 36: Performance Results: NVM to PMM
For most workloads, eliminating OS/FS code and buffering improves performance greatly on top of the NVM Baseline system
(even when DRAM is eliminated from the system)
Notes: grep and grep -r are CPU-intensive, so the change is not as large

## Slide 37: Performance Results
The workloads that see the greatest improvement from using a Persistent Memory are those that spend a large portion of their time executing system call code due to the two-level storage model

## Slide 38: Energy Results

## Slide 39: Energy Results: HDD to NVM
Between HDD-based and NVM-based systems, lower NVM energy leads to greatly reduced energy consumption

## Slide 40: Energy Results: NVM to PMM
Between systems with and without OS/FS code, energy improvements come from:
1. reduced code footprint, 2. reduced data movement
Large energy reductions with a PMM over the NVM based system
Notes: Reduced code footprint lowers *both* static and dynamic energy consumption by reducing number of instructions required to perform the same amount of work
Reduced data movement lowers static energy consumption

## Slide 41: Scalability Analysis: Effect of PMM Latency
Even if each PMM access takes a non-overlapped 50 cycles (conservative),
PMM still provides an overall improvement compared to the NVM baseline
Future research should target keeping PMM latencies in check
Notes: Up until this point, we have assumed that the PMM requires no additional overhead in order to explore the potential of systems with persistent memory. This figure shows how execution time varies as the latency *per memory access* to the PMM is varied from 1 to 100 cycles. Note that this estimate is conservative in the sense that it does not consider the potential for overlapping multiple access latencies in the PMM.
For each benchmark, the categories are normalized to the performance of the NVM Baseline system, shown on the left.

## Slide 42: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 43: Related Work
We provide a comprehensive overview of past work related to single-level stores and persistent memory techniques
  Integrating file systems with persistent memory
    Need optimized hardware to fully take advantage of new technologies
  Programming language support for persistent objects
    Incurs the added latency of indirect data access through software
  Load/store interfaces to persistent storage
    Lack efficient and fast hardware support for address translation, efficient file indexing, fast reliability and protection guarantees
  Analysis of OS overheads with Flash devices
    Our study corroborates findings in this area and shows even larger consequences for systems with emerging NVM devices
The goal of our work is to provide cheap and fast hardware support for memories to enable high energy efficiency and performance

## Slide 44: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 45: New Questions and Challenges
We identify and discuss several open research questions
Q1. How to tailor applications for systems with persistent memory?
Q2. How can hardware and software cooperate to support a scalable, persistent single-level address space?
Q3. How to provide efficient backward compatibility (for two-level stores) on persistent memory systems?
Q4. How to mitigate potential hardware performance and energy overheads?
Notes: (Say *in words* some of the talking points from the paper):
Q1. How should data be intelligently partitioned among devices?
How can data be efficiently transmitted between devices?
How can software be designed for improved fault tolerance?
How does persistent memory change models for availability?
Q2. What is the right interface between persistent memory and software?
What types of hooks and access data should be exposed to the software?
How can software signal to hardware that applications have particular access patterns?
How can software help provide consistency, reliability, and protection among heterogeneous devices?
Q3. How to efficiently support legacy system functionality (e.g., run HDD Baseline code on Persistent Memory and have it run nearly as fast as code designed for the Persistent Memory system)
How can devices in a persistent memory efficiently manage legacy interface (e.g., filesystem, page table) metadata?
Q4. A key challenge will be to keep accesses to a persistent memory fast, how this can be done efficiently (e.g., in between 10 to 50 cycles per access) is an important open area for future research.

## Slide 46: Outline
Background: Storage and Memory Models
Motivation: Eliminating Operating/File System Bottlenecks
Our Proposal: Hardware/Software Coordinated Management of Storage and Memory
  Opportunities and Benefits
Evaluation Methodology
Evaluation Results
Related Work
New Questions and Challenges
Conclusions

## Slide 47: Summary and Conclusions
Traditional two-level storage model is inefficient in terms of performance and energy
  Due to OS/FS code and buffering needed to manage two models
  Especially so in future devices with NVM technologies, as we show
New non-volatile memory based persistent memory designs that use a single-level storage model to unify memory and storage can alleviate this problem
We quantified the performance and energy benefits of such a single-level persistent memory/storage design
  Showed significant benefits from reduced code footprint, data movement, and system software overhead on a variety of workloads
Such a design requires more research to answer the questions we have posed and enable efficient persistent memory managers
   can lead to a fundamentally more efficient storage system

## Slide 48: Thank you.

## Slide 49: A Case for Efficient Hardware/Software Cooperative Management of Storage and Memory
Justin Meza*, Yixin Luo*, Samira Khan*†, Jishen Zhao§,
Yuan Xie§‡, and Onur Mutlu*
*Carnegie Mellon University
§Pennsylvania State University
†Intel Labs ‡AMD Research