## Slide 1: On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-Core Interconnects
George Nychis✝, Chris Fallin✝,
Thomas Moscibroda★, Onur Mutlu✝, Srinivasan Seshan✝
Carnegie Mellon University ✝
Microsoft Research Asia ★
Notes: What I’m going to talk to you about today is the on-chip network,
One such area where we can sort of expand that tent here at sigcomm
Which is a very unique type of network, due to different constraints,
Trying to take a network with hundreds to thousands of routers, cram it
Despite this uniqueness, t it has traditional networking problems, e.g., in this talk: congestion and scalability
** Unique design likely to require novel solutions to these traditional problems

## Slide 2: What is the On-Chip Network?
Multi-core Processor (9-core)
Cores
Memory
Controllers
GPUs
Cache
Banks
Notes: What you have in a multi-core processor are several components that require communication
Interestingly, there’s a discussion going on in the architecture community that we’re all familiar with
Recent studies have shown that a bufferless NoC can reduce energy and the area required
The bufferless NoC will be the focus of our talk for these reasons, and we’ll show that
One of the most important trends in computer architecture in the past decade has been this move towards chip multiprocessors, referred to as the CMP
Today’s smaller CMPs with 2 to 8 cores , the connectivity between these components has been the common bus
The solution taken by the architecture community was to move away from common bus and towards the on-chip network
----- Meeting Notes (8/10/12 15:21) -----
- congestion becomes the focus of our talk
- several alternatives, the NoC is a popular one
- citations
-

## Slide 3: What is the On-Chip Network?
Multi-core Processor (9-core)
Router
Network
Links
S
D
Notes: What you have in a multi-core processor are several components that require communication
Interestingly, there’s a discussion going on in the architecture community that we’re all familiar with
Recent studies have shown that a bufferless NoC can reduce energy and the area required
The bufferless NoC will be the focus of our talk for these reasons, and we’ll show that
One of the most important trends in computer architecture in the past decade has been this move towards chip multiprocessors, referred to as the CMP
Today’s smaller CMPs with 2 to 8 cores , the connectivity between these components has been the common bus
The solution taken by the architecture community was to move away from common bus and towards the on-chip network
----- Meeting Notes (8/10/12 15:21) -----
- congestion becomes the focus of our talk
- several alternatives, the NoC is a popular one
- citations
-

## Slide 4: Networking Challenges
On-Chip Network
Familiar discussion in the architecture community, e.g.:
  How to reduce congestion
  How to scale the network
  Choosing an effective topology
  Routing and buffer size
All historical problems in our field…
Notes: What you have in a multi-core processor are several components that require communication
Interestingly, there’s a discussion going on in the architecture community that we’re all familiar with
Recent studies have shown that a bufferless NoC can reduce energy and the area required
The bufferless NoC will be the focus of our talk for these reasons, and we’ll show that
One of the most important trends in computer architecture in the past decade has been this move towards chip multiprocessors, referred to as the CMP
Today’s smaller CMPs with 2 to 8 cores , the connectivity between these components has been the common bus
The solution taken by the architecture community was to move away from common bus and towards the on-chip network
----- Meeting Notes (8/10/12 15:21) -----
- congestion becomes the focus of our talk
- several alternatives, the NoC is a popular one
- citations
-

## Slide 5: Can We Apply Traditional Solutions? (1)
Routing min. complexity:
X-Y-Routing,
low latency
On-Chip Network (3x3)
Links links cannot be over-provisioned
Coordination global is often less expensive
Different constraints: unique network design
Different workloads: unique style of traffic and flow
S
D
X
Zoomed In
Bufferless Area: -60% Power: -40%
Notes: But the thing with the on-chip network is that it has a unique design, driven by different constraints and workloads.
Many of these constraints are driven by the fact that we’re trying to take a router that, even if you think of a
Simple home router is this big
----- Meeting Notes (8/10/12 14:23) -----
bufferless: why
- blue has got to go
----- Meeting Notes (8/10/12 15:21) -----
- benefits of bufferless
- only primarily considering bufferless in this talk
- global coordination is often practical, single domain.
* coming up with a central mechanism that works for the known topology
-

## Slide 6: Can We Apply Traditional Solutions? (2)
Zoomed In
Architecture
Network Layer
Router
Insn.
i5
i6
i7
i8
i9
(Instruct. Win)
Closed-Loop Instruction Window Limits In-Flight Traffic Per-Core
Different constraints: unique network design
Different workloads: unique style of traffic and flow
Routing min. complexity:
X-Y-Routing,
low latency
Coordination global is often less expensive
Links links cannot be over-provisioned
Bufferless Area: -60% Power: -40%
R5
R7
R8
Notes: What have at arch is a win that operates and similarly to sliding windows we’re all familiar with,
although size of this win does not shrink or grow.
allow mult insns run in parallel, any insn needs ext mem to exec
will require a request packet. Similar to the a traditional sliding window, window cannot slide until the respones (e.g., ACKs with needed mem)
until then, win cannot shift and core stalled. So what this does is create a closed loop system, and the maximum
Amount of traffic or req per-core limited to the size of window
----- Meeting Notes (8/10/12 15:21) -----
- greatly simplify this example
- don't animate the whole thing
----- Meeting Notes (8/16/12 12:35) -----
don't mention TCP- talk about it traditional sliding window
remove insn win

## Slide 7: Traffic and Congestion
On-Chip Network
S1
S2
D
age is initialized
0
1
Arbitration: oldest pkt first (dead/live-lock free)
0
2
1
contending for top port, oldest first, newest deflected
Injection only when output link is free
Manifestation of Congestion
Deflection: arbitration causing non-optimal hop
Notes: There are other characteristics of the network design chosen by the architecture community which impact the traffic and workload
Let me illustrate this with an example of traffic being generated by S1 and S2, both destined for D

## Slide 8: Traffic and Congestion
Can’t inject packet without a free port
Starvation: when a core cannot inject (no loss)
Definition: Starvation rate is a fraction of starved cycles
Arbitration: oldest pkt first (dead/live-lock free)
Injection only when output link is free
Manifestation of Congestion
Deflection: arbitration causing non-optimal hop
On-Chip Network
Notes: Another key property of bufferless NoCs is starvation
Let’s take this example where these 4 cores want to send
----- Meeting Notes (8/10/12 15:21) -----
- bullet points, 1 or 2: you either get ____ or ____
- get rid of the equation
- Buferless NoC Traffic and Congestion

## Slide 9: Outline
Bufferless On-Chip Networks: Congestion & Scalability
  Study of congestion at network and application layers
  Impact of congestion on scalability
Novel application-aware congestion control mechanism
Evaluation of congestion control mechanism
  Able to effectively scale the network
  Improve system throughput up to 27%
Notes: These properties under congestion motivate our study to understand how they impact the efficiency of the network and system, and its ability to scale
As we will show, congestion limits the system's efficiency, and prevents it from scaling effectively
This motivates the need for a novel congestion control mechanism, which we later show is able to restore scalability and improve throughput up to 27%
----- Meeting Notes (8/10/12 15:21) -----
Study capital
- title style capitalization

## Slide 10: Congestion and Scalability Study
Prior work: moderate intensity workloads, small on-chip net
  Energy and area benefits of going bufferless
  throughput comparable to buffered
Study: high intensity workloads & large network (4096 cores)
  Still comparable throughput with the benefits of bufferless?
Use real application workloads (e.g., matlab, gcc, bzip2, perl)
  Simulate the whole chip, including NoC
  Simulator used to publish in ISCA, MICRO, HPCA, NoCs…
Notes: ----- Meeting Notes (8/10/12 15:21) -----
Prior Work, existing state of the art - citation "prior work has shown"

## Slide 11: Congestion at the Network Level
Evaluate 700 different appl. mixes in 16-core system
Finding: net latency remains stable with congestion/deflects
  Unlike traditional networks
What about starvation rate?
Starvation increases significantly with congestion
Finding: starvation likely to impact performance; indicator of congestion
Each point represents a single workload
700%
Increase
Increase in network latency under congestion is only ~5-6 cycles
25%
Increase
Notes: By mixing application workloads, we can observe workloads with low, moderate, and high levels of traffic to understand the impact of congestion
----- Meeting Notes (8/10/12 12:23) -----
starvation as high as 32%
----- Meeting Notes (8/10/12 14:23) -----
equivalent in terms of importance, but see a lot more starvation17
----- Meeting Notes (8/10/12 15:21) -----
- traditionally, was an indicator of congestion
- call out closed-loop
- can go back, where do these delays creep in
- priority routing (guarantee a bound on the amount of deflections)
-

## Slide 12: Congestion at the Application Level
Define system throughput as sum of instructions-per-cycle (IPC) of all applications in system:
Unthrottle apps in single wkld
Sub-optimal
with congestion
Finding 1: Throughput decreases under congestion
Finding 2: Self-throttling of cores prevents collapse
Finding 3: Static throttling can provide some gain (e.g., 14%), but we will show up to 27% gain with app-aware throttling
Throughput Does Not Collapse
Throttled
Unthrottled
Notes: We perform the following expiriment. We take a sample 4x4, and start by throttling all applications by 100%
At some point before the applications are running freely and the level of congestion is lower, the system has a greater level of throughput… therefore, letting the applications run freely creates congestion and decreases throughput
----- Meeting Notes (8/10/12 14:23) -----
- get some of the gain from application awareness
- key understanding of why starvation
----- Meeting Notes (8/10/12 15:21) -----
- highlight there are no points beyond
- put the network
- draw as lines
- can't push the utilization any further
- not using different configurations
- instruction window, just remove it (insns win)

## Slide 13: Impact of Congestion on Scalability
Prior work: 16-64 cores Our work: up to 4096 cores
As we increase system’s size:
  Starvation rate increases
    A core can be starved up to 37% of all cycles!
  Per-node throughput decreases with system’s size
    Up to 38% reduction
Notes: ----- Meeting Notes (8/10/12 14:11) -----
- could move earlier, with a buffered line
----- Meeting Notes (8/10/12 14:23) -----
- buffered allow you to avoid starvation and deflection
----- Meeting Notes (8/10/12 15:21) -----
- locality needs to be explained
- when you have a distributed system, always trying to localize for performance reasons
- Model instead of introduce, messages/fragments travel 3 hops
- messages have to go a certain distance, 95% is not the amount of data on the core
- google for map reduce locality
- pheonix

## Slide 14: Summary of Congestion Study
Network congestion limits scalability and performance
  Due to starvation rate, not increased network latency
  Starvation rate is the indicator of congestion in on-chip net
Self-throttling nature of cores prevent congestion collapse
Throttling: reduced congestion, improved performance
  Motivation for congestion control
Congestion control must be application-aware
Notes: The key things that we showed through our study was that congestion ultimately limited the scalability and performance of the network
And unlike in traditional networks, this is due to increases in starvation rate and not increases in network latency

## Slide 15: Outline
Bufferless On-Chip Networks: Congestion & Scalability
  Study of congestion at network and application layers
  Impact of congestion on scalability
Novel application-aware congestion control mechanism
Evaluation of congestion control mechanism
  Able to effectively scale the network
  Improve system throughput up to 27%
Notes: Given the serious consideration towards a bufferless design,

## Slide 16: Developing a Congestion Controller
Traditional congestion controllers designed to:
  Improve network efficiency
  Maintain fairness of network access
  Provide stability (and avoid collapse)
  Operate in a distributed manner
A controller for on-chip networks must:
  Have minimal complexity
  Be area-efficient
  We show: be application-aware
When
Considering:
On-Chip Network
…in paper: global and simple controller
Notes: When designing a congestion controller, there have traditionally been 4 key properties the controller is designed to provide
Providing a level of stability in the network traffic
Operate in distributed manner for deployability
However, when considering a NoC: these design decisions change
For example, the self-throttling nature of the cores has already been shown to prevent collapse and provide a level of stability
----- Meeting Notes (8/10/12 15:21) -----
- think about improving network efficiency
-grey these out in the paper

## Slide 17: Need For Application Awareness
Finding 3: different applications respond differently to an increase in network throughput (unlike gromacs, mcf barely gains)
Throttling reduces congestion, improves system throughput
  Under congestion, what core should be throttled?
Use 16-core system, alternate 90% throttle rate to applications
Finding 1: the app that is throttled impacts system performance
Unlike traditional congestion controllers (e.g., TCP): cannot be application agnostic
Finding 2: application throughput does not dictate whom to throttle
-9%
+21%
+33%
<1%
1.3
0.6
Notes: It’s important to know the behavior of the application on the core being throttled
when designing a congestion controller, the key question in terms of efficiency is: who do we throttle and by what ammount
So what we needed was a study to understand how different applications responded to throttling in this closed-loop system.
To gain insight, we constructed a 4x4 NoC with two applications.
If we choose to throttle gromacs _____, if we choose to throttle mcf ______
----- Meeting Notes (8/10/12 15:21) -----
- three stacked bars
- three bars incrementally
- Efficiency Component
- Application-Aware throttling
----- Meeting Notes (8/16/12 12:35) -----
distributing the applications evenly across 16 core system, 8 instances of each
with 90% probability, we delay each memory req by 1 cycle

## Slide 18: Instructions-Per-Packet (IPP)
Key Insight: Not all packets are created equal
  more L1 misses  more traffic to progress
Phase behavior on the order of millions of cycles
  Throttling during a “high” IPP phase will hurt performance
Since L1 miss rate varies over execution, IPP is dynamic
IPP only depends on the L1 miss rate
  independent of the level of congestion & execution rate
  low value: need many packets shift window
  provides the application-layer insight needed
Instructions-Per-Packet (IPP) = I/P
Notes: Unlike the TCP window, networking traffic isn’t needed for every entry in that window to shift it
Only when the needed memory is external does an application need network access to progress
If you think back to our instruction window, if only one instruction required external memory, only a small amount of traffic is needed to progress
We compute IPF for our 26 application workloads
  MCF’s IPF: 0.583, Gromacs IPF: 12.41
  IPF explains MCF and Gromacs throttling experiment
----- Meeting Notes (7/11/12 17:57) -----
what an instruction window
"retire" --> closed loop, can't progress window
--- limited window of instructions being stalled and waiting to
- it can't move, which creates a level of architectural congestion control
- quick comparison to TCP…
* why it doesn't collapse
- have to go over the network when you have an L1 miss
----- Meeting Notes (8/10/12 14:23) -----
- flit to fragment
- remove instructions per flit or fragment10
----- Meeting Notes (8/10/12 15:21) -----
-develop an interval based controller
- title: how often to throttle

## Slide 19: Instructions-Per-Packet (IPP)
Since L1 miss rate varies over execution, IPP is dynamic
  Throttling during a “high” IPP phase will hurt performance
IPP provides application-layer insight in who to throttle
  Dynamic IPP  Throttling must be dynamic
When congested: throttle applications with low IPP
Fairness: scale throttling rate by application’s IPP
  Details in paper show that fairness in throttling
Notes: We compute IPF for our 26 application workloads
  MCF’s IPF: 0.583, Gromacs IPF: 12.41
  IPF explains MCF and Gromacs throttling experiment
----- Meeting Notes (7/11/12 17:57) -----
what an instruction window
"retire" --> closed loop, can't progress window
--- limited window of instructions being stalled and waiting to
- it can't move, which creates a level of architectural congestion control
- quick comparison to TCP…
* why it doesn't collapse
- have to go over the network when you have an L1 miss

## Slide 20: Outline
Bufferless On-Chip Network: Congestion & Scalability
  Study of congestion at network and application layers
  Impact of congestion on scalability
Novel application-aware congestion control mechanism
Evaluation of congestion control mechanism
  Able to effectively scale the network
  Improve system throughput up to 27%
Notes: Given the serious consideration towards a bufferless design,

## Slide 21: Evaluation of Improved Efficiency
Evaluate with 875 real workloads (700 16-core, 175 64-core)
  generate balanced set of CMP workloads (cloud computing)
Network Utilization With No Congestion Control
The improvement in system throughput for workloads
Improvement up to 27% under congested workloads
Does not degrade non-congested workloads
Only 4/875 workloads have perform. reduced > 0.5%
Do not unfairly throttle applications down (in paper)

## Slide 22: Evaluation of Improved Scalability
Comparison points…
  Baseline bufferless: doesn’t scale
  Buffered: area/power expensive
Contribution: keep area and power benefits of bufferless, while achieving comparable performance
  Application-aware throttling
  Overall reduction in congestion
Power consumption reduced through increase in net efficiency
Many other results in paper, e.g., Fairness, starvation, latency…
Notes: ----- Meeting Notes (8/10/12 14:10) -----
- needs to be clear on the separation of buffered and bufferless
- our own line in color
- could be like bridging the gap
----- Meeting Notes (8/10/12 15:21) -----
- put the benefits of buffered of bufferless earlier on
- more details on what the comparison points are

## Slide 23: Summary of Study, Results, and Conclusions
Highlighted a traditional networking problem in a new context
  Unique design requires novel solution
We showed congestion limited efficiency and scalability, and that self-throttling nature of cores prevents collapse
Study showed congestion control would require app-awareness
Our application-aware congestion controller provided:
  A more efficient network-layer (reduced latency)
  Improvements in system throughput (up to 27%)
  Effectively scale the CMP (shown for up to 4096 cores)
Notes: ----- Meeting Notes (7/11/12 17:57) -----
comparison with buffered at the end,
- why not just do buffered again?
- saving from the starvation
- compared to an expensive buffered, forego everything for scaling in the future
----- Meeting Notes (8/10/12 15:21) -----
- can bold some things
- traditional problems, different solution
- can put it on a separate slide

## Slide 24: Discussion
Congestion is just one of many similarities, discussion in paper, e.g.,
  Traffic Engineering: multi-threaded workloads w/ “hotspots”
  Data Centers: similar topology, dynamic routing & computation
  Coding: “XOR’s In-The-Air” adapted to the on-chip network:
    i.e., instead of deflecting 1 of 2 packets, XOR the packets and forward the combination over the optimal hop
Notes: Latency: off-chip is 10micro, instead of 50ns
Power: power constraints are much different
Complexity: on-chip you’re more limited by wires and their layout
Traffic patterns: off-chip network applications are catered understanding network latencies

## Slide 25: Low-Complexity & Area-Efficient Controller
Global interval-based controller, simple & low hardware req
  Only every 100k cycles: who to throttle, and by what rate
Information needed from cores:
  Starvation Rate: detect congestion
  IPF: who to throttle, and rate
Comm. with controller is in-band, control packets include needed info
Hardware: only 149-bits per core
  minimal compared to 128KB L1
CMP
Zoomed In
(to a single core)
IPF: 2 Counters + Divider
Insns Retired
Flits Injected
Starvation Rate: Shift Reg + Comparator
/
Router
…
1
0
0
0
1
1
…
Throttler: Counter + Comparator
Injection Permitted?
Notes: How to create an efficient controller in terms of system throughput
But, as previously mentioned, a NoC controller must also be low in complexity and area-efficient

## Slide 26: Evaluation of Fairness
Controller does not unfairly throttle low IPF applications

## Slide 27: Breakdown by Workload
Break the results down by the application “mix”
  H=High, M=Medium, L=Low … and mixes of such workloads
As expected, majority of benefits come from heavier workloads
Do not unfairly throttle down lower intensity workloads
Improvements greater in larger sized network (8x8)