## Slide 1: Accelerating Genome Analysis A Primer on an Ongoing Journey
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
18 June 2022
AACBB Workshop Keynote @ ISCA 2022

## Slide 2: Overview
System design for bioinformatics is a critical problem
  It has large scientific, medical, societal, personal implications
This talk is about accelerating a key step in bioinformatics: genome sequence analysis
  In particular, read mapping
Many bottlenecks exist in accessing and manipulating huge amounts of genomic data during analysis
We will cover various recent ideas to accelerate read mapping
  My personal journey since September 2006

## Slide 3: Our Dream (circa 2007)
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
  Which of these DNAs does this DNA segment match with?
  What is the likely genetic disposition of this patient to this drug?
  What disease/condition might this particular DNA/RNA piece associated with?
  . . .

## Slide 4: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 5: A Few Overview Readings (I)
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose,
Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey”
IEEE Micro, August 2020.
https://arxiv.org/pdf/2008.00961.pdf

## Slide 6: A Few Overview Readings (II)
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]
https://arxiv.org/pdf/2106.06433.pdf

## Slide 7: A Few Overview Readings (III)
https://arxiv.org/pdf/2205.07957.pdf

## Slide 8: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 9: What Is a Genome Made Of?
Cell
Nucleus
The discovery of DNA’s double-helical structure (Watson+, 1953)
Notes: Unlocking the life’s code requires diving into the nucleus of our body cells, where the double-stranded genome resides. Genome is literally the 'code of life' - it is the set of instructions for making everything from you to zebras, strawberries, and even yeast.
since the discovery of dna’s double-helical structure (watson et al. 1953)

## Slide 10: The Central Dogma of Molecular Biology
Phenotypes
Genotypes
Notes: Our DNA is literally a cookbook that contains the information needed to make all of our phenotypes and traits. Our genes are the recipes for making us what we are physically.

## Slide 11: DNA Under Electron Microscope
human chromosome #12
from HeLa’s cell
Notes: Henrietta Lacks,

## Slide 12
CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCC
GGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTG

## Slide 13: How Large is a Genome?
Phi X174 virus
5.386 Kilo bp
E. coli O157:H7
5.44 Million bp
Homo Sapiens
3.2 Billion bp
Onion, Allium Cepa
16 Billion bp
Paris Japonica
149 Billion bp
Notes: Phi x174 is a virus that Infects E. Coli bacteria
You may be exposed to E. coli from contaminated water or food — especially raw vegetables and undercooked ground beef.
Paris Japonica : A rare Japanese flower
============================
Phi is 600K time smaller than the genome of human
E coli is ~600 time smaller than the human genome
Onion has a genome that is 5x larger than that of human
Paris japonica’s genome is 46x larger than the human genome

## Slide 14: DNA Sequencing
Goal:
  Find the complete sequence of A, C, G, T’s in an organism’s DNA
Challenge:
  There is no machine that takes long DNA as an input, and gives the complete sequence as output
  All sequencing machines chop DNA into pieces and identify relatively small pieces (but not how they fit together)

## Slide 15: Genome Sequencing
Large DNA molecule
Small DNA fragments
Reads
ACGTACCCCGT
GATACACTGTG
TTTTTTTAATT
CTAGGGACCTT
ACGACGTAGCT
AAAAAAAAAA
ACGAGCGGGT
Notes: As the whole genome of most organisms cannot be sequenced all at once, the genome is broken into smaller fragments.
After each fragment is sequenced, small pieces of DNA sequences (i.e. reads) are generated.

## Slide 16: Genome Sequencing and Analysis
Current sequencing machines provide
small randomized fragments
of the original DNA sequence
Alser+, "Technology dictates algorithms: Recent developments in read alignment", Genome Biology, 2021
Read Mapping
Reads

## Slide 17: Untangling Yarn Balls & DNA Sequencing
Notes: untangling yarn ball

## Slide 18
Genome Sequencers
… and more! All produce data with different properties.
Roche/454
Illumina HiSeq2000
Ion Torrent PGM
Ion Torrent Proton
AB SOLiD
Oxford Nanopore GridION
Oxford Nanopore MinION
Complete
Genomics
Illumina MiSeq
Pacific Biosciences RS
Illumina
NovaSeq
6000

## Slide 19: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION

## Slide 20: The Genomic Era
1990-2003: The Human Genome Project (HGP) provides a complete and accurate sequence of all DNA base pairs that make up the human genome and finds 20,000 to 25,000 human genes.
13 year-long
$3,000,000,000 (in 1991 USD)
Notes: The 13-year long human project is the starting of the genomic era! It opened the door to remarkable biomedical discoveries by providing the first complete human genome sequence. It cost 3 billion dollars to read the entire sequence.

## Slide 21: The Genomic Era (continued)
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 22: Genome Sequencing Cost Is Reducing
*From NIH (https://www.genome.gov/about-genomics/fact-sheets/DNA-Sequencing-Costs-Data)

## Slide 23: Genome Sequencing Cost Is Reducing
*From NIH (https://www.genome.gov/about-genomics/fact-sheets/DNA-Sequencing-Costs-Data)

## Slide 24: High-Throughput Sequencing (HTS)
= Second Generation
= Next Generation
= Massively Parallel Sequencing
= High Throughput Sequencing (HTS) = Sequencing by Synthesis (Illumina)
flow cell
Notes: Second generation = next generation = massively parallel sequencing = high throughput sequencing (HTS) = Sequencing by Synthesis
Attach large number of DNA molecules to the flow cell then sequence by synthesis using CMOS light sensor to observe the chemical interactions

## Slide 25: High-Throughput Sequencing (HTS)
A
C
G
C
C
C
G
T
G
C
G
T
A
C
G
T
A
C
G
T
A
C
G
C
A
C
G
T
A
A
G
A
A
C
G
T
A
C
G
T
A
C
G
T
A
C
G
A
A
C
G
T
A
C
G
T
A
C
G
T
G
C
G
G
A
C
G
T
A
C
G
T
A
C
G G G C
G
C
G
C
G
T
A
C
G
C
A
C
G
T
A
C
G
T
A
C
G
T
A
C
G
T
T
T
T
T
A
C
G
T
T
G
C
A
Glass flow cell surface
As a workaround, HTS technologies sequence random short DNA fragments (75-300 basepairs long) of copies of the original molecule.
The sequencer adds the molecule “T”
to all bases near the flow cell surface and
observes the chemical reaction via a CMOS sensor.
If a reaction happens then the base is “A”
Notes: Until today, there is no machine takes genomic sample and produces the full sequence of the donor. I
nstead, HTS technology is used to sequence/read random short DNA fragments of copies of the original molecule.
The sequencer adds the molecule “T” to all bases near the flow cell surface and observes the chemical reaction by a CMOS sensor. If a reaction happens then the base is “A” (A reacts with T, C with G and vice versa).
This step is repeated for A, C, and G molecules for each base of the fragments.
Bases are sequenced concurrently, hence the name “high throughput”.

## Slide 26: High-Throughput Sequencing
Massively parallel sequencing technology
  Illumina, Roche 454, Ion Torrent, SOLID…
Small DNA fragments are first amplified and then sequenced in parallel, leading to
  High throughput
  High speed
  Low cost
  Short reads
Sequencing is done by either reading optical signals as each base is added, or by detecting hydrogen ions instead of light, leading to:
  Low error rates (relatively)
  Reads lack information about their order and which part of genome they are originated from

## Slide 27: Solving the Puzzle
https://www.pacb.com/smrt-science/smrt-sequencing/hifi-reads-for-highly-accurate-long-read-sequencing/
Sequenced Reads
Reference genome
.FASTA file
.FASTQ file
Notes: Rhinoceros

## Slide 28: Newer Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version] [Slides (pptx) (pdf)] [Talk Video at AACBB 2019]
Oxford Nanopore MinION

## Slide 29: Types of Genomic Reads
Wenger+, "Accurate circular consensus long-read sequencing improves variant detection and assembly of a human genome", Nature Biotechnology, 2019
But still very expensive!
https://labs.wsu.edu/genomicscore/illumina-sequencing/
https://pacbio.gs.washington.edu/
Long: 10-20 kb
Accurate: 99.8%
Notes: By sequencing the same DNA segment many times (10 to 30 times), we can have accurate more longer reads.

## Slide 30
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 31: Read Mapping Techniques in 111 Pages
Mohammed Alser, Jeremy Rotman, Dhrithi Deshpande, Kodi Taraszka, Huwenbo Shi, Pelin Icer Baykal, Harry Taegyun Yang, Victor Xue, Sergey Knyazev, Benjamin D. Singer, Brunilda Balliu, David Koslicki, Pavel Skums, Alex Zelikovsky,
Can Alkan, Onur Mutlu, Serghei Mangul
"Technology dictates algorithms: Recent developments in read alignment"
Genome Biology, 2021
[Source code]
In-depth analysis of 107 read mappers (1988-2020)

## Slide 32: Why Do We Care?

## Slide 33
Example Question: If I give you a bunch of sequences, tell me where they are the same and where they are different.
Multiple sequence alignment

## Slide 34: Genome Sequence Alignment: Example
Source: By Aaron E. Darling, István Miklós, Mark A. Ragan - Figure 1 from Darling AE, Miklós I, Ragan MA (2008).
"Dynamics of Genome Rearrangement in Bacterial Populations". PLOS Genetics. DOI:10.1371/journal.pgen.1000128., CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=30550950

## Slide 35: The Genetic Similarity Between Species
99.9%
96%
Human ~ Chimpanzee
Human ~ Human
90%
Human ~ Cat
80%
Human ~ Cow
50-60%
Human ~ Banana

## Slide 36: Finding Variations Associated with Traits
…ACATGCCGACATTTCATAGGCC…
…ACATGCCGACATTTCATAAGCC…
…ACATGCCGACATTTCATAGGCC…
…ACATGCCGACATTTCATAAGCC…
…ACATGCCGACATTTCATAGGCC…
…ACATGCCGACATTTCATAGGCC…
…ACATGCCGACATTTCATAAGCC…
…ACATGCCGACATTTCATAAGCC…
…ACATGTCGACATTTCATAGGCC…
…ACATGTCGACATTTCATAAGCC…
…ACATGTCGACATTTCATAGGCC…
…ACATGTCGACATTTCATAAGCC…
…ACATGTCGACATTTCATAGGCC…
…ACATGTCGACATTTCATAAGCC…
…ACATGTCGACATTTCATAGGCC…
…ACATGTCGACATTTCATAAGCC…
SNP1 SNP2 Blood Pressure
180
175
170
165
160
145
140
130
120
120
115
110
110
110
105
100
Eleazar Eskin: Discovering the Causal Variants Involved in GWAS Studies, CGSI 2018, UCLA
Individual #1
Individual #2
Individual #3
Individual #4
Individual #5
Individual #6
Individual #7
Individual #8
Individual #9
Individual #10
Individual #11
Individual #12
Individual #13
Individual #14
Individual #15
Individual #16
SNP: single nucleotide polymorphism
Notes: Genetic association study is a procedure of seeking for the SNPs potentially causing the phenotypic changes. Here in this example of blood pressure, it appears that the left SNP is more strongly associated with the blood pressure than the right SNP, because all the individual with genotype “C” have high blood pressure, and individuals with “T” has low blood pressure.

## Slide 37: Genome-Wide Association Studies (GWAS)
Enables detection of genetic variants associated with phenotypes using two groups of people.
Manhattan plot
variant with higher frequency in cases than in controls
https://onlinelearning.hms.harvard.edu/hmx/courses/genetic-testing/
Notes: the negative logarithm of the association p-value for each single nucleotide polymorphism (SNP) displayed on the Y-axis, meaning that each dot on the Manhattan plot signifies a SNP

## Slide 38: SNPs and Personalized Medicine
https://opensnp.org/snps/rs12979860

## Slide 39: Much Larger Structural Variations
AUTISM
Weiss, N Eng J Med 2008
Deletion of 593 kb
OBESITY
Walters, Nature 2010
Deletion of 593 kb
SCHIZOPHRENIA
McCarthy, Nat Genet 2009
Duplication of 593 kb
UNDERWEIGHT
Jacquemont, Nature 2011
Duplication of 593 kb
Deletion in the short arm
of chromosome 16 (16p11.2)
Duplication in the short arm
of chromosome 16 (16p11.2)
CNV: copy number variation
Notes: SNP is 1 bp, INDEL 1-49bp, Structural Variation >=50bp
https://www.nejm.org/doi/full/10.1056/NEJMoa075974
https://www.ncbi.nlm.nih.gov/pmc/articles/PMC2880448/

## Slide 40: Personalized Medicine for Critically Ill Infants
Farnaes+, “Rapid whole-genome sequencing decreases infant morbidity and cost of hospitalization”, NPJ Genomic Medicine, 2018
rWGS can be performed in 2-day (costly) or 5-day time to interpretation.
Diagnostic rWGS for infants
  Avoids morbidity
  Reduces hospital stay length by 6%-69%
  Reduces inpatient cost by $800,000-$2,000,000.
Notes: There is also an urgent need for rapidly incorporating clinical sequencing into clinical practice for diagnosis of genetic disorders in critically ill infants [53, 54, 55, 56]. While early diagnosis in such infants shortens the clinical course and enables optimal outcomes [57, 58, 59], it is still challenging to deliver ecient clinical sequencing for tens to hundreds of thousands of hospitalized infants each year [60].

## Slide 41: Recommended Reading
Ho+, "Structural variation in the sequencing era", Nature Reviews Genetics, 2020

## Slide 42
Metagenomics, genome assembly, de novo sequencing
http://math.oregonstate.edu/~koslickd
uncleaned de Bruijn graph
Question 2: Given a bunch of short sequences, Can you identify the approximate species cluster for genomically unknown organisms (bacteria)?
Notes: organism detection in metagenomes

## Slide 43: Population-Scale Microbiome Profiling
https://blog.wego.com/7-crowded-places-and-events-that-you-will-love/

## Slide 44: City-Scale Microbiome Profiling
Afshinnekoo+, "Geospatial Resolution of Human and Bacterial Diversity with City-Scale Metagenomics", Cell Systems, 2015
Notes: In 2015, they sequenced DNA from surfaces across the entire New York City (NYC) subway system.
~ 1,700 microbial taxa detected were dominated mostly by human skin bacteria.
Almost half the DNA present on the subway surfaces matched no known organism.
And though results showed that the bacteria found in the subways were mostly harmless, they detected pathogenic agents, including fragments of the plague and anthrax genomes !!
MegaBLAST-LCA Pipeline The MegaBLAST-LCA pipeline consisted of five steps explained in detail below.
Paired-end reads were prepared for BLAST by trimming, filtering on quality scores, and converting to unpaired FASTA sequences.
Prepared reads were searched for in the NCBI NT database using MegaBLAST (default parameters).
MegaBLAST hits were filtered such that short and low-scoring hits were ignored in subsequent analysis.
Reads with MegaBLAST hits to multiple taxa were assigned to the LCA taxa in the NCBI Taxonomy using the MEGAN algorithm. For example, hits to multiple species of the same genus are assigned to the common genus by the LCA algorithm.
Finally, for each sample, the total number of reads assigned to each taxon were counted. We validated our MegaBLAST-LCA pipeline on a mock community of 11 bacterial species (see Tables S2 and S3).

## Slide 45: Global-Scale Microbiome Profiling
Danko+, "A global metagenomic map of urban microbiomes and antimicrobial resistance", Cell, 2021

## Slide 46: A Tsunami of Sequencing Data
A Tera-scale increase in sequencing production in the past 25 years

## Slide 47: Another Question: Example from 2020-…
Source: https://nanoporetech.com/about-us/news/200-oxford-nanopore-sequencers-have-left-uk-china-support-rapid-near-sample

## Slide 48: Example: Scalable SARS-CoV-2 Testing
Bloom+, "Swab-Seq: A high-throughput platform for massively scaled up SARS-CoV-2 testing", medRxiv, 2020

## Slide 49: Example: Rapid Surveillance of Ebola Outbreak
Quick+, “Real-time, portable genome sequencing for Ebola surveillance”, Nature, 2016

## Slide 50: We Need Faster & Scalable Genome Analysis
Predicting the presence and relative abundance of microbes in a sample
Understanding genetic variations, species, evolution, …
Rapid surveillance of disease outbreaks
Developing personalized medicine
And, many, many other applications …
Notes: Knowing what organisms are present in a given environmental sample and how abundant are they

## Slide 51: One Problem

## Slide 52
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
300 M
bases/min
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Illumina HiSeq4000
2 M
bases/min
on average
(0.6%)
We Are Bottlenecked in Read Mapping
Notes: Typical sequencer machine generates a flood of reads, for example, Illumina HiSeq4000 generates 300 million bases/minute.
However, existing computer alignment algorithms can only process 0.6% of these reads in the same amount of time.
This gap is widening as more advanced sequencers are made available in the market.

## Slide 53: The Read Mapping Bottleneck
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Read Sequencing
Read Mapping
* BWA-MEM
** HiSeqX10, MinION
*
**
150x slower
Million
bases/minute
300
Million
bases/minute
2
Notes: 12.48
5.2 CPU hours
144x
60 CPU hours
BWA-MEM
25 minutes
Illumine HiSeq X10
25 minutes
Nanopore MinION
Short reads generated in a day using today’s HTS machines (e.g., Illumine HiSeq X10) can be mapped to the human reference genome using BWA-MEM [36], a popular and widely-used read mapper, in 12.5 CPU (central processing unit) days when running on a single core [66, 67]. BWA-MEM also takes about 2.5 CPU days to map long reads that are generated in 25 minutes using today’s Nanopore MinION sequencer [68]

## Slide 54: The Read Mapping Bottleneck
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Human whole
genomes
Human
1
Illumina NovaSeq 6000
48
at 30× coverage
in about 2 days
genome
32 CPU hours
on a 48-core processor
Chart: 
| Read Mapping | Others
Sales | 0.71 | 0.29
Goyal+, "Ultra-fast next generation human genome sequencing data processing using DRAGENTM bio-IT processor for precision medicine”, Open Journal of Genetics, 2017.
Notes: 12.48
5.2 CPU hours
144x
60 CPU hours
BWA-MEM
25 minutes
Illumine HiSeq X10
25 minutes
Nanopore MinION
Short reads generated in a day using today’s HTS machines (e.g., Illumine HiSeq X10) can be mapped to the human reference genome using BWA-MEM [36], a popular and widely-used read mapper, in 12.5 CPU (central processing unit) days when running on a single core [66, 67]. BWA-MEM also takes about 2.5 CPU days to map long reads that are generated in 25 minutes using today’s Nanopore MinION sequencer [68]

## Slide 55: Lack of Specialized Compute Capability
Special-Purpose Machine
for Sequencing
General-Purpose Machine
for Analysis
FAST SLOW

## Slide 56: One Problem
Need to construct
the entire genome
from many sequenced reads

## Slide 57: Genome Sequencing
Large DNA molecule
Small DNA fragments
Reads
ACGTACCCCGT
GATACACTGTG
TTTTTTTAATT
CTAGGGACCTT
ACGACGTAGCT
AAAAAAAAAA
ACGAGCGGGT
Notes: As the whole genome of most organisms cannot be sequenced all at once, the genome is broken into smaller fragments.
After each fragment is sequenced, small pieces of DNA sequences (i.e. reads) are generated.

## Slide 58: Genome Sequence Analysis
Read Mapping, method of aligning the reads against a known reference genome to detect matches and variations
ACGTACCCCGT
GATACACTGTG
TTTTTTTAATT
CTAGGGACCTT
ACGACGTAGCT
AAAAAAAAAA
ACGAGCGGGT
Reads
De novo Assembly, method of merging the reads in order to construct the original sequence (reference genome)
Reference
Genome
Original
Sequence
Notes: These reads can then be analyzed following two different approaches: read mapping and de novo assembly. Read mapping is the process of aligning the reads against the reference genome to detect variations in the sequenced genome. Reference genome is a DNA sequence accepted as the representation of the genomic sequence of a species. The genome of a species is copied from individual to individual across multiple generations of a population with minimal differences at every step. The genomes of different individuals of the same species have typically the same number of chromosomes and most of the same bases in each chromosome. Thus, we can talk about a reference genome of a species.
De novo assembly is the method of combining the reads to construct the original sequence when a reference genome does not exist.

## Slide 59: Read Mapping
Map many short DNA fragments (reads) to a known reference genome with some differences allowed
Reference genome
Reads
DNA, logically
DNA, physically
Mapping short reads to reference genome is challenging (billions of 50-300 base pair reads)
Notes: Read mapping is a post processing procedure after DNA sequencing. It maps the data output from a DNA sequencer, which are many short DNA fragments, to a known reference genome, with some minor differences allowed.
To illustrate the problem better, let us take a closer look at the DNA itself. Logically, the DNA is a double stranded long string. In reality, within a cell they folded into a sphere in the nucleus like a ball of wool. Since it is very hard to disentangle the DNA at molecular level, to extract the information out, a sequencer cuts the mass into many short DNA pieces which are called reads.
A mapper’s job is to find where these DNA short reads are most likely to be originally placed so that later we can assemble them in the correct order to restore the original DNA.
Mapping these short reads, up to billions of them, with each one being 50 to 300 base-pairs long, to the reference genome is challenging.

## Slide 60: Read Mapping for Metagenomic Analysis
Reference Database
Reads
“text format”
genetic material recovered directly from environmental samples
Reads from different unknown donors at sequencing time are mapped to many known reference genomes
Notes: Read mapping is a post processing procedure after DNA sequencing. It maps the data output from a DNA sequencer, which are many short DNA fragments, to a known reference genome, with some minor differences allowed.
To illustrate the problem better, let us take a closer look at the DNA itself. Logically, the DNA is a double stranded long string. In reality, within a cell they folded into a sphere in the nucleus like a ball of wool. Since it is very hard to disentangle the DNA at molecular level, to extract the information out, a sequencer cuts the mass into many short DNA pieces which are called reads.
A mapper’s job is to find where these DNA short reads are most likely to be originally placed so that later we can assemble them in the correct order to restore the original DNA.
Mapping these short reads, up to billions of them, with each one being 50 to 300 base-pairs long, to the reference genome is challenging.

## Slide 61: Read Mapping Execution Time (Old Times)
Chart: 
| candidate alignment locations (CAL) | SIMD banded Levenshtein edit distance | SAM printing
Time (sec) | 3738.88 | 81368.0945 | 2269.8755
Notes: An overwhelming majority of the read mapper’s execution time is spent in read alignment.

## Slide 62: Matching Each Read to Reference Genome
Reference Genome .FASTA file:
Sequenced Reads .FASTQ file:

## Slide 63: Base-by-Base Comparison
Notes: (f) Once the pre-alignment filter accepts the alignment between a read and a region in the reference genome then DP-based (or non-DP based) verification algorithms are used to generate the alignment file (in BAM or SAM formats), which contains alignment information such as the exact number of differences, location of each difference, and their type.

## Slide 64: Read Alignment/Verification
Edit distance is defined as the minimum number of edits (i.e. insertions, deletions, or substitutions) needed to make the read exactly match the reference segment.
N | E | - | T | H | E | R | L | A | N | D | S
S | W | I | T | Z | E | R | L | A | N | D | -
NETHERLANDS x SWITZERLAND
match
deletion
insertion
mismatch
Notes: http://www.let.rug.nl/kleiweg/lev/

## Slide 65: Challenges in Read Mapping
Need to find many mappings of each read
  A short read may map to many locations, especially with High-Throughput DNA Sequencing technologies
  How can we find all mappings efficiently?
Need to tolerate small variances/errors in each read
  Each individual is different: Subject’s DNA may slightly differ from the reference (Mismatches, insertions, deletions)
  How can we efficiently map each read with up to e errors present?
Need to map each read very fast (i.e., performance is important)
  Human DNA is 3.2 billion base pairs long  Millions to billions of reads (State-of-the-art mappers take weeks to map a human’s DNA)
  How can we design a much higher performance read mapper?
Notes: There are three main challenges.
First. The mapper needs to find many mappings for each read. Because the read is so short, they can map to multiple locations in the reference genome. How can we efficiently find all mappings of a read?
Second. The mapper needs to tolerate small variance or errors in each read. Since individuals are different, the subject’s DNA might slightly differs from the reference DNA, which can be mismatches, insertions or deletions of base pairs. How can we efficiently map each read with up to a number of e errors present?
Third. The mapper needs to map each read very fast. In another word, performance is important. Because the human DNA is 3.2 billion base-pairs long and each read is only hundreds of base-pairs long, there can be billions of reads subjected to mapping for an individual human. Current state of the art mappers take weeks to map a human’s DNA. So the question is, how can we design a much higher performance read mapper?

## Slide 66: Why Is Read Alignment Slow?
Quadratic-time dynamic-programming algorithm(s)
etc
etc
Data dependencies limit the computation parallelism
Entire matrix computed even though strings may be dissimilar
etc
Notes: 1- Read alignment follows the basic dynamic-programming doctrine which runs in a quadratic time.
2- Data dependencies between the entries limits the parallelism. Each cell depends or three pre-computed cells (immediate left, upper, and upper-left cells). Thus, we can compute the vectors one after another but not in parallel. Left-to-right, or top-to-bottom, anti-diagonal.
3- We can solve a significant amount of time, If we can find a way to detect the incorrect mappings with cheap heuristics, much cheaper than computing the alignment.

## Slide 67: Example: Dynamic Programming Table
 |  | N | E | T | H | E | R | L | A | N | D | S
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
S | 1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 10
W | 2 | 2 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
I | 3 | 3 | 3 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
T | 4 | 4 | 4 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Z | 5 | 5 | 5 | 4 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
E | 6 | 6 | 5 | 5 | 5 | 4 | 5 | 6 | 7 | 8 | 9 | 10
R | 7 | 7 | 6 | 6 | 6 | 5 | 4 | 5 | 6 | 7 | 8 | 9
L | 8 | 8 | 7 | 7 | 7 | 6 | 5 | 4 | 5 | 6 | 7 | 8
A | 9 | 9 | 8 | 8 | 8 | 7 | 6 | 5 | 4 | 5 | 6 | 7
N | 10 | 9 | 9 | 9 | 9 | 8 | 7 | 6 | 5 | 4 | 5 | 6
D | 11 | 10 | 10 | 10 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 5
NETHERLANDS x SWITZERLAND
immediate left,
upper left,
upper entries of its own
Notes: 1- Read alignment follows the basic dynamic-programming doctrine which runs in a quadratic time.
2- Data dependencies between the entries limits the parallelism. Each cell depends or three pre-computed cells (immediate left, upper, and upper-left cells). Thus, we can compute the vectors one after another but not in parallel. Left-to-right, or top-to-bottom, anti-diagonal.
3- We can solve a significant amount of time, If we can find a way to detect the incorrect mappings with cheap heuristics, much cheaper than computing the alignment.

## Slide 68: Example: Dynamic Programming Table
 |  | N | E | T | H | E | R | L | A | N | D | S
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
S | 1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 10
W | 2 | 2 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
I | 3 | 3 | 3 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
T | 4 | 4 | 4 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Z | 5 | 5 | 5 | 4 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
E | 6 | 6 | 5 | 5 | 5 | 4 | 5 | 6 | 7 | 8 | 9 | 10
R | 7 | 7 | 6 | 6 | 6 | 5 | 4 | 5 | 6 | 7 | 8 | 9
L | 8 | 8 | 7 | 7 | 7 | 6 | 5 | 4 | 5 | 6 | 7 | 8
A | 9 | 9 | 8 | 8 | 8 | 7 | 6 | 5 | 4 | 5 | 6 | 7
N | 10 | 9 | 9 | 9 | 9 | 8 | 7 | 6 | 5 | 4 | 5 | 6
D | 11 | 10 | 10 | 10 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 5
Matrix-filling is O(mn) time and space.
Backtrace is O(m + n) time.
NETHERLANDS x SWITZERLAND
Notes: 1- Read alignment follows the basic dynamic-programming doctrine which runs in a quadratic time.
2- Data dependencies between the entries limits the parallelism. Each cell depends or three pre-computed cells (immediate left, upper, and upper-left cells). Thus, we can compute the vectors one after another but not in parallel. Left-to-right, or top-to-bottom, anti-diagonal.
3- We can solve a significant amount of time, If we can find a way to detect the incorrect mappings with cheap heuristics, much cheaper than computing the alignment.

## Slide 69: Example: Dynamic Programming
 |  | N | E | T | H | E | R | L | A | N | D | S
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
S | 1 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 10
W | 2 | 2 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
I | 3 | 3 | 3 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
T | 4 | 4 | 4 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
Z | 5 | 5 | 5 | 4 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
E | 6 | 6 | 5 | 5 | 5 | 4 | 5 | 6 | 7 | 8 | 9 | 10
R | 7 | 7 | 6 | 6 | 6 | 5 | 4 | 5 | 6 | 7 | 8 | 9
L | 8 | 8 | 7 | 7 | 7 | 6 | 5 | 4 | 5 | 6 | 7 | 8
A | 9 | 9 | 8 | 8 | 8 | 7 | 6 | 5 | 4 | 5 | 6 | 7
N | 10 | 9 | 9 | 9 | 9 | 8 | 7 | 6 | 5 | 4 | 5 | 6
D | 11 | 10 | 10 | 10 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 5
Quadratic-time dynamic-programming algorithm
etc
etc
Data dependencies limit the computation parallelism
Entire matrix is computed even though strings can be dissimilar
etc
WHY?!
NETHERLANDS x SWITZERLAND
NETHERLANDS x S
NETHERLANDS x SW
NETHERLANDS x SWI
NETERLANDS x SWIT
NETHERLANDS x SWITZ
NETHERLANDS x SWITZE
NETHERLANDS x SWITZER
NETHERLANDS x SWITZERL
NETHERLANDS x SWITZERLA
NETHERLANDS x SWITZERLAN
NETHERLANDS x SWITZERLAND
Enumerate all possible prefixes
Notes: 1- Read alignment follows the basic dynamic-programming doctrine which runs in a quadratic time.
2- Data dependencies between the entries limits the parallelism. Each cell depends or three pre-computed cells (immediate left, upper, and upper-left cells). Thus, we can compute the vectors one after another but not in parallel. Left-to-right, or top-to-bottom, anti-diagonal.
3- We can solve a significant amount of time, If we can find a way to detect the incorrect mappings with cheap heuristics, much cheaper than computing the alignment.

## Slide 70: Computational Cost is Mathematically Proven
https://arxiv.org/abs/1412.0348

## Slide 71: Read Mapping Techniques in 111 Pages
Mohammed Alser, Jeremy Rotman, Dhrithi Deshpande, Kodi Taraszka, Huwenbo Shi, Pelin Icer Baykal, Harry Taegyun Yang, Victor Xue, Sergey Knyazev, Benjamin D. Singer, Brunilda Balliu, David Koslicki, Pavel Skums, Alex Zelikovsky,
Can Alkan, Onur Mutlu, Serghei Mangul
"Technology dictates algorithms: Recent developments in read alignment"
Genome Biology, 2021
[Source code]
In-depth analysis of 107 read mappers (1988-2020)

## Slide 72: Read Mapping Execution Time (Modern)
ONT FASTQ size: 103MB (151 reads), Mean length: 356,403 bp, std: 173,168 bp, longest length: 817,917 bp
Chart: 
| KSW2 | Seed Chaining | Sorting Seeds | Collect Matching Seeds | Collect Minimizers
Sales | 0.46 | 0.16 | 0.29 | 0.08 | 0.02
>60%
of the read mapper’s execution time is spent in sequence alignment
minimap2

## Slide 73: Accelerating Read Mapping
Alser+, “Accelerating Genome Analysis: A Primer on an Ongoing Journey”, IEEE Micro, 2020.

## Slide 74: Detailed Analysis of Tackling the Bottleneck
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose,
Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey”
IEEE Micro, August 2020.

## Slide 75: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 76: Read Mapping Algorithms: Two Styles
Hash based seed-and-extend (hash table, suffix array, suffix tree)
  Index the “k-mers” in the genome into a hash table (pre-processing)
  When searching a read, find the location of a k-mer in the read; then extend through alignment
  More sensitive (can find all mapping locations), but slow
  Requires large memory; this can be reduced with cost to run time
Burrows-Wheeler Transform & Ferragina-Manzini Index based aligners
  BWT is a compression method used to compress the genome index
  Perfect matches can be found very quickly, memory lookup costs increase for imperfect matches
  Reduced sensitivity

## Slide 77: Hash Table Based Read Mappers
Key Idea
  Preprocess the reference into a Hash Table
  Use Hash Table to map reads

## Slide 78: Hash Table-Based Mappers [Alkan+ Nature Gen’09]
12 | 324 | 577 | 940
AAAAAAAAAAAA
AAAAAAAAAAAC
AAAAAAAAAAAT
13 | 421 | 412 | 765 | 889
......
CCCCCCCCCCCC
......
24 | 459 | 744 | 988 | 989
......
......
TTTTTTTTTTTT
36 | 535 | 123
NULL
Reference genome
k-mer or 12-mer
(string of length k)
Location list—where the k-mer
occurs in reference gnome
Once for a reference
Notes: In preprocessing, the mapper stores the full permutations of a short fixed-length DNA string called k-mers, with k denoting the length of the string. In this example, k = 12 and they are also called 12-mers. For each k-mer, the mapper sweeps through the reference genome and stores all of the occurrence locations of the k-mer into a location list. The mapper then do this for all k-mers. If a permutation never appeared in the reference genome, there will be an empty list for it.
This data structure, usually implemented as the hash table is only constructed once for a reference genome

## Slide 79: Hash Table Based Read Mappers
Key Idea
  Preprocess the reference into a Hash Table
  Use Hash Table to map reads

## Slide 80: Hash Table-Based Mappers [Alkan+ Nature Gen’09]
12
12 | 324 | 557 | 940
AAAAAAAAAAAACCCCCCCCCCCCTTTTTTTTTTT
CCCCCCCCCCCC
TTTTTTTTTTTT
Reference Genome
Hash Table (HT)
read
k-mers
AAAAAAAAAAAA
CCCCCCCCCCCC
TTTTTTTTTTTT
24 | 459 | 744 | 988 | 989
36 | 535 | 823
…AAAAAAAAAAAACCCCCCCCCCCCTTTTTTTTTTTT…
AAAAAAAAAAAACCCCCCCCCCCCTTTTTTTTTTTT
AAAAAAAAAAAA
324
.. AAAAAAAAAAAAAACGCTTCCACCTTAATCTGGTTG..
read
***
..****************************************..
Invalid mapping
Valid mapping
✔
Verification/Local Alignment
Notes: For a single read, the mapper first divides the read into non-overlapping k-mers, and uses the k-mers to query the hash table. The hash table returns the locations lists of the k-mers and traverses them one by one.
For each location in the list, the mapper retrieves the reference sequence at the location from the database and verifies if the read differs from the reference with more than e errors. The verification itself, is an expensive string comparison (edit distance computation) function. It compares the two DNA strings base pair by base pair, until the end. Then the mapper moves on to the next step, repeats, until it examined all locations.
This is the best previous work circa 2013.

## Slide 81: Our First Step: Comprehensive Mapping
+ Guaranteed to find all mappings  sensitive
+ Can tolerate up to e errors
http://mrfast.sourceforge.net/
Alkan+, "Personalized copy number and segmental duplication
maps using next-generation sequencing”, Nature Genetics 2009.
Notes: It turned out the Hash Table based mappers solve the first 2 challenges pretty well. They guarantee to find all mappings with no more than e errors present.

## Slide 82: Problem and Goal
Poor performance of existing read mappers: Very slow
  Verification/alignment takes too long to execute
  Verification requires a memory access for reference genome + many base-pair-wise comparisons between the reference and the read (edit distance computation)
Goal: Speed up the mapper by reducing the cost of verification
Chart: 
| Execution time (s)
Verification | 17451
Other | 918
95%
Notes: It turns out the performance of existing hash table based mappers is very poor. They are very slow.
This is because of the expensive verification computation. To perform a verification, the mapper has to access the memory once for the reference genome and conduct many base-pair wise comparisons between the reference genome and the read, in order to locate the errors.
In fact, from our profiling result, the verification process can consume up to 95% of the execution time. Moreover, most of the verification calculations are unnecessary.
Our goal is to speedup the mapper by reducing the execution time of the verification process.

## Slide 83: Overarching Key Idea
Filter fast before you align
Minimize costly
edit distance computations
(“approximate string comparisons”)

## Slide 84: Overarching Key Idea
Sequenced Reads
Similar to Reference
Too Dissimilar to Reference
Focus processing power
on these
(e.g., edit distance comp.)
Quickly find these
and filter them out
w/o costly computation

## Slide 85: Accelerating Genome Analysis: Overview
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 86: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 87: Our First Filter: Pure Software Approach
Download the source code and try for yourself
  Download link to FastHASH
Xin+, "Accelerating Read Mapping with FastHASH", BMC Genomics 2013.

## Slide 88: Reducing the Cost of Verification
Most verification (edit distance computation) calculations are unnecessary
  1 out of 1000 potential locations passes the verification process
We can get rid of unnecessary verification calculations by
  Detecting and rejecting early invalid mappings (filtering)
  Reducing the number of potential mappings to examine
Notes: How can we do that? It turns out most of the verification calculations are unnecessary. We observe that usually only 1 out of 1000 potential mapping locations passes the verification process becoming a valid mapping.
We also observe that we can get rid of unnecessary verification calculations by
Detecting and rejecting early invalid mappings
and by Reducing the number of potential mappings

## Slide 89: Key Observations [Xin+, BMC Genomics 2013]
Observation 1
  Adjacent k-mers in the read should also be adjacent in the reference genome
  Read mapper can quickly reject mappings that do not satisfy this property
Observation 2
  Some k-mers are cheaper to verify than others because they have shorter location lists (they occur less frequently in the reference genome)
    Mapper needs to examine only e+1 k-mers’ locations to tolerate e errors
  Read mapper can choose the cheapest e+1 k-mers and verify their locations
Notes: Observation 1: For valid mappings, Adjacent k-mers in the read should also be adjacent in the reference genome.
Hence, mapper can quickly reject mappings that do not satisfy this property.
Observation 2: Some k-mers are cheaper than others because they have shorter location lists, which means they occur less frequently in the reference genome. Previous work proved that the mapper only needs to examine e+1 k-mers’ locations to tolerate e errors.
Hense, the mapper can choose the cheapest e+1 k-mers and verify their locations.

## Slide 90: FastHASH Mechanisms [Xin+, BMC Genomics 2013]
Adjacency Filtering (AF): Rejects obviously invalid mapping locations at early stage to avoid unnecessary verifications
Cheap K-mer Selection (CKS): Reduces the absolute number of potential mapping locations to verify
Notes: In our work, FastHASH, we have two mechanisms to leverage the two observations respectively.
Mechanism 1: Adjacency Filtering, which ….
Mechanism 2: Cheap k-mer Selection, which ….
Let us first take a look at Adjacency Filtering.

## Slide 91: Adjacency Filtering (AF)
Goal: detect and filter out invalid mappings at early stage
Key Insight: For a valid mapping, adjacent k-mers in the read are also adjacent in the reference genome
Key Idea: search for adjacent locations in the k-mers’ location lists
  If more than e k-mers fail  there must be more than e errors  invalid mapping
AAAAAAAAAAAACCCCCCCCCCCCTTTTTTTTTTT
read
Reference genome
Valid mapping
Invalid mapping
Notes: The goal of AF is to detect invalid mappings at early stage.
This is based on the insight that, for a valid mapping, adjacent k-mers in the read are also adjacent in the reference genome.
Let’s take a look at the previous example. The read is divided into 3 k-mers and they occur at different locations in the reference genome
From the figure, we can see that, only the location in the blue box is a valid mapping, as the three adjacent k-mers of the read are adjacent in the reference genome. Other locations are all invalid mappings because they only map to a single isolated k-mers from the read.
The key idea is instead of performing the expensive verification calculation, we can search for adjacent locations in the k-mers’ location lists and if more than e k-mers fail this process, we know there must be more than e errors present, concluding that the mapping is invalid

## Slide 92: Adjacency Filtering (AF)
12
12 | 324 | 557 | 940
AAAAAAAAAAAACCCCCCCCCCCCTTTTTTTTTTT
CCCCCCCCCCCC
TTTTTTTTTTTT
Reference Genome
Hash Table (HT)
read
k-mers
AAAAAAAAAAAA
CCCCCCCCCCCC
TTTTTTTTTTTT
24 | 459 | 744 | 988 | 989
36 | 535 | 123
…AAAAAAAAAAAACCCCCCCCCCCCTTTTTTTTTTTT…
AAAAAAAAAAAACCCCCCCCCCCCTTTTTTTTTTTT
AAAAAAAAAAAA
324
24?
36?
336?
***
+12
+24
557
569?
940
952?
✗
Notes: Let us look back to the previous example. With Adjacency Filtering, we still traverse the location lists but with each location, before the verification, we check if adjacent locations are in adjacent k-mers’ location lists.
In this case, with location 12 from the first k-mer, and the k-mer length being 12, we will be looking for location 24 in the second k-mer’s location lists, which is there and the third k-mer’s location list, which is also there. Because all adjacent locations are found in adjacent k-mers, we pass location 12 towards the verification process.
For the next location, 324, we search for adjacent location 336 in 2nd k-mer and it’s not there. We conclude there must be at least an error and skip the verification process and move on to the next location 577. We search for adjacent location 589, which is also not there. Then we move to the next 940 and search for 952, which is also not there. So on and so forth for all locations. In this way, we only do verification once and that is for the single valid mapping of this read.

## Slide 93: FastHASH Mechanisms [Xin+, BMC Genomics 2013]
Adjacency Filtering (AF): Rejects obviously invalid mapping locations at early stage to avoid unnecessary verifications
Cheap K-mer Selection (CKS): Reduces the absolute number of potential mapping locations to verify
Notes: In our work, FastHASH, we have two mechanisms to leverage the two observations respectively.
Mechanism 1: Adjacency Filtering, which ….
Mechanism 2: Cheap k-mer Selection, which ….
Let us first take a look at Adjacency Filtering.

## Slide 94: Cheap K-mer Selection (CKS)
Goal: Reduce the number of potential mappings to examine
Key insight:
  K-mers have different cost to examine: Some k-mers are cheaper as they have fewer locations than others (occur less frequently in reference genome)
Key idea:
  Sort the k-mers based on their number of locations
  Select the k-mers with the fewest number locations to verify
Notes: The goal of Cheap K-mer Selection is to reduce the number of potential mappings
The key insight is that the k-mers have different cost to examine. Some k-mers are cheaper as they have fewer locations in their location lists than others, which also means they occur less frequently in the reference genome.
The key idea is to sort the k-mers based on their number of locations and select the k-mers with fewest locations to verify.

## Slide 95: Cheap K-mer Selection
e=2 (examine 3 k-mers)
AAGCTCAATTTC CCTCCTTAATTT TCCTCTTAAGAA GGGTATGGCTAG AAGGTTGAGAGC CTTAGGCTTACC
read
314
1231
4414
9219
4 loc.
338
…
…
…
…
1K loc.
376
…
…
…
…
2K loc.
326
1451
2 loc.
326
1451
2 loc.
388
…
…
…
…
1K loc.
Previous work needs to verify:
3004 locations
FastHASH verifies only:
8 locations
Locations
Number of Locations
Cheapest 3 k-mers
Expensive 3 k-mers
Notes: In this example, we have a longer read which can be divided into 6 k-mers. The error tolerance threshold e is set to 2, which means we need to select at least 3 k-mers to verify their locations.
Here is the location list of a k-mer. The first several entries here are locations while the last entry summarizes the number of locations of this k-mer.
We can see that for this read, some of the k-mers are cheap, having fewer than 10 locations, whereas some of them are expensive, having morethan thousands of locations.
Previous work selects k-mers at uniform locations, hence verifying 3004 locations. FastHASH however, selects only the cheap k-mers and verifies only 6 locations.

## Slide 96: Methodology
Implemented FastHASH on top of state-of-the-art mapper: mrFAST
  New version mrFAST-2.5.0.0 over mrFAST-2.1.0.6
Tested with real read sets generated from Illumina platform
  1M reads of a human (160 base pairs)
  500K reads of a chimpanzee (101 base pairs)
  500K reads of a orangutan (70 base pairs)
Tested with simulated reads generated from reference genome
  1M simulated reads of human (180 base pairs)
Evaluation system
  Intel Core i7 Sandy Bridge machine
  16 GB of main memory
Notes: We implemented FastHASH on top of state-of-the-art mapper mrFAST, updating it to a new version 2.5
We evaluated the algorithm on two data sets.
Data set one are real read sets generated from illumina platform.
Data set two are simulated read sets generated from the reference genome.
All the evaluations were obtained from an Intel Core i7 Sandy Bridge machine with 16GB of main memory

## Slide 97: FastHASH Speedup: Entire Read Mapper
orangutan
simulated
human
chimpanzee
19x
With FastHASH, new mrFAST obtains up to 19x speedup over previous version, without losing valid mappings
Notes: Here we present the performance result of FastHASH, which is the speedup verses the old mrFAST.
We run the program with different error threshold e.
And the x axis shows the error threshold e.
The y axis shows the times of speedup.
The data is obtained with different read sets as well.
From this graph, we can see that With FastHASH, mrFAST obtains up to 19x speedup over previous version.

## Slide 98: Analysis
Reduction of potential mappings with FastHASH
99%
99%
99%
99%
99%
FastHASH filters out over 99% of the potential mappings without sacrificing any valid mappings
Notes: This graph shows where the speedup comes from.
In this graph, we show the reduction of potential mappings with FastHASH. The x axis shows the error threshold e and the y axis shows the number of potential mappings. Notice that y axis is log10 scaled.
With FastHASH, we observe that over 99% of the potential mappings are filtered out at low cost, reducing a large amount of verification calculation.

## Slide 99: FastHASH Summary & Conclusion
Problem: Existing read mappers perform poorly, especially in the presence of errors
Observation: Most of the verification (edit distance) calculations are unnecessary  filter them out
Key Idea: Exploit the structure of the genome to
  Reject invalid mappings early (Adjacency Filtering)
  Reduce the number of possible mappings to examine (Cheap K-mer Selection)
Key Result: FastHASH obtains up to 19x speedup over the state-of-the-art mapper without losing valid mappings
Notes: In this work, we talked about the problem, which is poor performance of existing read mappers to map billion of short reads to the reference genome, in the presence of errors.
We made the observation that most of the verification calculations are unnecessary.
The key idea of FastHASH is to reduce the cost of unnecessary verification calculations.
We have 2 mechanisms:
The first one rejects invalid mappings early, which is AF.
  The second one Reduces the number of possible mappings to examine, which is Cheap K-mer Selection
  As a result, we achieved up to 19x speedup over previous state-of-the-art mapper

## Slide 100: More on FastHASH
Download source code and try for yourself
  Download link to FastHASH
Xin+, "Accelerating Read Mapping with FastHASH", BMC Genomics 2013.

## Slide 101: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 102: Shifted Hamming Distance: SIMD Acceleration
Xin+, "Shifted Hamming Distance: A Fast and Accurate SIMD-friendly Filter
to Accelerate Alignment Verification in Read Mapping”, Bioinformatics 2015.
https://github.com/CMU-SAFARI/Shifted-Hamming-Distance

## Slide 103: Shifted Hamming Distance
Key observation:
  If two strings differ by E edits, then every bp match can be aligned in at most 2E shifts (of one of the strings).
    Insight: Shifting a string by one “corrects” for one “error”
Key idea:
  Compute “Shifted Hamming Distance”: AND of 2E Hamming Distances of two strings, to filter out invalid mappings
    Uses bit-parallel operations that nicely map to SIMD instructions
Key result:
  SHD is 3x faster than SeqAn (the best implementation of Gene Myers’ bit-vector algorithm), with only a 7% false positive rate
  The fastest CPU-based filtering (pre-alignment) mechanism
Notes: To the best of our knowledge, SHD is the fastest CPU-based filter. It depends on the fact the a deleted character causes all trailing characters to be shifted to the left direction. To correctly pairwise compare this sequence, we need to shift it back to the right direction then compare. Generally we need 2E shifts to compare any two sequences regardless the edit is insertion or deletion.
GateKeeper is another recent filter that uses FPGA to improve the speed and the read length support of SHD.

## Slide 104: Hamming Distance ()
I
S
T
A
N
B
U
L
I
S
T
A
N
B
U
L
8 matches 0 mismatches
3 matches 5 mismatches
To cancel the effect of a deletion, we need to shift in the right direction
Edit = 1 Deletion
Notes: Our second proposed method to accelerate read mappers is to parallelize the matrix computation.
To explain our new matrix, here is an example of exact match sequences. Now imagine there is a base deletion for any reason.

## Slide 105: Insight: Shifting a String Helps Similarity Search
I
S
T
A
N
B
U
L
I
S
T
N
B
U
L
3 matches 5 mismatches
To cancel the effect of the deletion, we need to shift in the right direction
Notes: After deletion, the trailing bases will be shifted to left to form a single sequence.
But when we align it back, we get too many mismatches though the number of edits is only ONE.
To cancel the effect of deletion and correctly align the sequences, we have to shift the sequence to right and align again.

## Slide 106: Insight: Shifting a String Helps Similarity Search
I
S
T
A
N
B
U
L
I
S
T
N
B
U
L
7 matches 1 mismatch
I
S
T
N
B
U
L
Notes: With the help of another right-shifted copy of the original sequence, we can have more similarities between the two sequences. Think about other scenarios where you have an insertion? Or a combination of deletion and insertion?

## Slide 107: Shifted Hamming Distance
I
S
T
N
B
U
L
7 matches 1 mismatch
XOR
XOR
AND
Edit = 1 Deletion
I
S
T
N
B
U
L
0
0
0
1
1
1
1
0
0
0
0
1
1
1
0 0 0 1 0 0 0 0
Count 1’s
I
S
T
A
N
B
U
L
Notes: With the help of another right-shifted copy of the original sequence, we can have more similarities between the two sequences. Think about other scenarios where you have an insertion? Or a combination of deletion and insertion?

## Slide 108: Highly Parallel Matrix Computation
We need to compute 2E+1 vectors, E=edit distance threshold
dp[i][j]= 0 if X[i]=Y[j]
1 if X[i]≠Y[j]
No data dependencies!
2 Deletion Hamming masks
2 Insertion Hamming masks
Reference
Query
Notes: So this is how we compute the filter matrix. We pairwise compare each character from a sequence to its corresponding character from the other sequence. Match =0, Mismatch=1
The yellow diagonal vector represents XOR between the two sequences. The pink diagonal vectors represent right-shifted copies of the query sequence then compared to the reference. The blue vectors represent left-shifted copies of the query. By this we can guarantee that we can correctly examine any two sequences regardless the type of edits they have. AND NO DATA DEPENDENCIES between the cells.

## Slide 109: Key Idea of SHD Filtering
Generate 2E+1 masks
Amend random zeros:
101  111 & 1001  1111
AND all masks,
ACCEPT iff number of ‘1’ ≤ Threshold
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 110: Alignment vs. Pre-alignment (Filtering)
|dp[i][j-1] -1 // Inser.
dp[i][j]=max|dp[i-1][j] -1 // Del.
|dp[i-1][j-1]-1 // Subs.
|dp[i-1][j-1]+0 // match.
dp[i][j]=|0 if X[i]=Y[j]
|1 if X[i]≠Y[j]
No data dependencies!
Each cell depends on three pre-computed cells!
Needleman-Wunsch Neighborhood Map
where 1≤ i ≤ m
i-E ≤ j ≤ i+E
1
1
0
Our goal is to track the diagonally consecutive matches
in the neighborhood map
Notes: How to achieve a filter that is even much faster than the banded alignment algorithm?
1- Removing the data dependencies between the cells of the dynamic programming matrix.
In NW algorithm, each cell depends on three pre-computed cells (top, diagonal, and left cells). This restricts the way we computed the entire matrix (left to right, or top to bottom, or anti-diagonal), which limits the parallelism effort. In GateKeeper, we just perform a pairwise comparison (ZERO means a match and ONE means a mismatch). NO data dependencies in GateKeeper!!
2- Generating a binary matrix and backtrack the solution using only bitwise operations.

## Slide 111: Alignment Matrix vs. Neighborhood Map
|dp[i][j-1] -1 // Inser.
dp[i][j]=max|dp[i-1][j] -1 // Del.
|dp[i-1][j-1]-1 // Subs.
|dp[i-1][j-1]+0 // match.
dp[i][j]=|0 if X[i]=Y[j]
|1 if X[i]≠Y[j]
No data dependencies!
Each cell depends on three pre-computed cells!
Needleman-Wunsch Neighborhood Map
where 1≤ i ≤ m
i-E ≤ j ≤ i+E
1
1
0
Our goal to track the diagonally consecutive matches in the neighborhood map.
Independent vectors can be processed in parallel using hardware technologies
DRAM Layers
Logic Layer
Notes: How to achieve a filter that is even much faster than the banded alignment algorithm?
1- Removing the data dependencies between the cells of the dynamic programming matrix.
In NW algorithm, each cell depends on three pre-computed cells (top, diagonal, and left cells). This restricts the way we computed the entire matrix (left to right, or top to bottom, or anti-diagonal), which limits the parallelism effort. In GateKeeper, we just perform a pairwise comparison (ZERO means a match and ONE means a mismatch). NO data dependencies in GateKeeper!!
2- Generating a binary matrix and backtrack the solution using only bitwise operations.

## Slide 112: New Bottleneck: Filtering (Pre-Alignment)
Sequencing generates many reads, each of which potentially mapping to many locations

Filtering (Pre-alignment) eliminates the need to verify/align read to invalid mapping locations

Alignment/verification (costly edit distance computation) is performed only on reads that pass the filter
New bottleneck in read mapping becomes the “filtering (pre-alignment)” step

## Slide 113: More on Shifted Hamming Distance
Xin+, "Shifted Hamming Distance: A Fast and Accurate SIMD-friendly Filter
to Accelerate Alignment Verification in Read Mapping”, Bioinformatics 2015.
https://github.com/CMU-SAFARI/Shifted-Hamming-Distance

## Slide 114: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 115: Location Filtering (Pre-alignment)
Alignment is expensive
  We need to align millions to billions of reads
  Modern read mappers reduce the time spent on alignment for increased performance. Can be done in two ways:
    Optimize the algorithm for alignment
    Reduce the number of alignments necessary by filtering out mismatches quickly
  Both methods are used by mappers today, but filtering has replaced alignment as the bottleneck [Xin+, BMC Genomics 2013]
Notes: [CLICK]
Alignment is the algorithm for determining a match between a read and a reference substring. This is very expensive and requires the use of an O(n2) dynamic programming algorithm.
[CLICK]
To give the scale of required computation, a single human can generate millions to billions of reads, and each read results in multiple locations
[CLICK]
Modern read mappers reduce the time spent on alignment for increased performance. This can be done in two ways:
[CLICK]
By further optimizing the alignment algorithm, which many prior works have done.. OR
[CLICK]
By reducing the number of alignments necessary by quickly discarding mismatches. We refer to this as filtering.
[CLICK]
Both methods are used by mappers today, but now filtering has replaced alignment as the bottleneck.
[CLICK]
Our goal is to improve the filtering step in read mappers
[END-CLICK]

## Slide 116: Location Filtering (Pre-alignment)
Alignment is expensive
  We need to align millions to billions of reads
  Modern read mappers reduce the time spent on alignment for increased performance. Can be done in two ways:
    Optimize the algorithm for alignment
    Reduce the number of alignments necessary by filtering out mismatches quickly
  Both methods are used by mappers today, but filtering has replaced alignment as the bottleneck [Xin+, BMC Genomics 2013]
Our goal is to accelerate read mapping
by improving the filtering step
Notes: [CLICK]
Alignment is the algorithm for determining a match between a read and a reference substring. This is very expensive and requires the use of an O(n2) dynamic programming algorithm.
[CLICK]
To give the scale of required computation, a single human can generate millions to billions of reads, and each read results in multiple locations
[CLICK]
Modern read mappers reduce the time spent on alignment for increased performance. This can be done in two ways:
[CLICK]
By further optimizing the alignment algorithm, which many prior works have done.. OR
[CLICK]
By reducing the number of alignments necessary by quickly discarding mismatches. We refer to this as filtering.
[CLICK]
Both methods are used by mappers today, but now filtering has replaced alignment as the bottleneck.
[CLICK]
Our goal is to improve the filtering step in read mappers
[END-CLICK]

## Slide 117: Ideal Location Filtering Algorithm
Filters out most of the incorrect mappings
Preserves all correct mappings
Does this quickly
Step 2
Query the Index
Step 3
Read Alignment
Notes: Ideal pre-alignment filter should be both accurate and fast:
1- Faster than typical aligners to compensate the computation overhead introduced by its filtering technique (as we added an extra filtering stage).
2- We define the accuracy of pre-alignment filtering as follows: It’s the ability of the filter to reject most of the incorrect mappings (i.e., maximizing the true reject rate and minimizing the false accept rate) while keeping all the correct ones (i.e., zero false reject rate).

## Slide 118: Location Filtering Example
Filter
894
37
1564
140
1203
1564
894
1203
37
140
Hash Table
Read Sequence (100 bp)
✔
Reference Genome
140
1203
1564
Aligning
.
.
.
Match!
Aligning
.
.
.
Mismatch
✘
✘
✘
False Accept
✘
Notes: [CLICK]
Again, we split the read into k-mers of length 5 and query the hash table for their location lists
[CLICK]
We then pass the locations through the filter and attempt to efficiently discard as many locations as possible before having to run alignment. Here we see that locations that are obviously mismatches get discarded, before needing alignment.
[CLICK]
The read must then be aligned against the strings that pass the filter to determine location matches
[CLICK]
Any location that passes through the filter, but then fails the alignment is called a false negative. False negative rates and filtering speed are important metrics for analyzing a filter.
note that when the filter was added, we were able to forego 3 instances of alignment thus saving us execution time.
[END-CLICK]

## Slide 119: Alignment vs. Pre-alignment (Filtering)
|dp[i][j-1] // Inser.
dp[i][j]=1+max|dp[i-1][j] // Del.
|dp[i-1][j-1]// Subs.
dp[i][j]=|0 if X[i]=Y[j]
|1 if X[i]≠Y[j]
No data dependencies!
Each cell depends on three pre-computed cells!
Needleman-Wunsch SHD
Independent vectors can be processed in parallel using hardware technologies
DRAM Layers
Logic Layer
Notes: How to achieve a filter that is even much faster than the banded alignment algorithm?
1- Removing the data dependencies between the cells of the dynamic programming matrix.
In NW algorithm, each cell depends on three pre-computed cells (top, diagonal, and left cells). This restricts the way we computed the entire matrix (left to right, or top to bottom, or anti-diagonal), which limits the parallelism effort. In GateKeeper, we just perform a pairwise comparison (ZERO means a match and ONE means a mismatch). NO data dependencies in GateKeeper!!
2- Generating a binary matrix and backtrack the solution using only bitwise operations.

## Slide 120
GateKeeper: FPGA-Based Alignment Filtering
Alignment Filter
st
1
FPGA-based Alignment Filter.
Notes: To bridge the widening gap between the sequencer & the mapper, we propose the concept of pre-alignment filtering. We added a new examination step before the accurate alignment step. The main objective of this step is to detect the incorrect mappings accurately and rapidly. Only the mappings that pass our filter are examined by the alignment step. We also explore exploiting todays’ hardware accelerators to further boost the filtering speed of such filters.

## Slide 121: GateKeeper: FPGA-Based Alignment Filtering
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 122: GateKeeper Walkthrough
Generate 2E+1 masks
Amend random zeros:
101  111 & 1001  1111
AND all masks,
ACCEPT iff number of ‘1’ ≤ Threshold
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 123: GateKeeper Walkthrough (cont’d)
Generate 2E+1 masks
Amend random zeros:
101  111 & 1001  1111
AND all masks,
ACCEPT iff number of ‘1’ ≤ Threshold
(2E+1)*(ReadLength) 5-input LUT.
E right-shift registers (length=ReadLength)
E left-shift registers (length=ReadLength)
(2E+1) * (ReadLength) 2-XOR operations.
(2E)*(ReadLength) 2-AND operations.
(ReadLength/4) 5-input LUT.
ReadLength-bit counter.
Notes: So basically we have three main steps in GateKeeper:
Step 1: Building the matrix that involves 2E shift registers (each diagonal bit-vector is generated by shifting the read then pairwise compare the shifted read with the reference), each of length =ReadLength.
Step 2: Cancelling the meaningless short zeros by changing them to ones (101 is changed to 111 and 1001 to 1111) using 5-input LUT of the VC709 FPGA.
Step 3: AND all vectors and count the number of zeros in the AND mask.
Alignment filters do not replace the alignment verification.
Alignment filters eliminate most of incorrect mappings.
Alignment filters keep the correct (or nearly correct) mappings.

## Slide 124: GateKeeper Accelerator Architecture
Maximum data throughput =~13.3 billion bases/sec
Can examine 8 (300 bp) or 16 (100 bp) mappings concurrently at 250 MHz
Occupies 50% (100 bp) to 91% (300 bp) of the FPGA slice LUTs and registers
Notes: Here, we present the architecture of GateKeeper. Each processing core is able to examine a single mapping in a single clock cycle. We integrate many hardware processing cores in the architecture of GateKeeper for examining many mappings in a parallel fashion. The input read-reference pairs are transferred from the host to the FPGA via PCIe third generation 4-lane at the rate of 13.3 billion bases/sec. With this data throughput, we can have 16 processing cores work concurrently to examine 16 read-reference pairs. Our architecture occupies only 50% of the FPGA resource for a read length of 100 bp and 91% for a read length of 300 bp.

## Slide 125: FPGA Chip Layout
Read length:
300 bp
Error threshold:
E=15

## Slide 126: GateKeeper vs. SHD
FPGA (Xilinx VC709)
Multi-core (parallel)
Examines a single mapping @ 125 MHz
Limited to PCIe Gen3(4x) transfer rate (128 bits @ 250MHz)
Amending requires:
  (2E+1) 5-input LUT.
Intel SIMD
Single-core (sequential)
Examines a single mapping @ ~2MHz
Limited to a read length of 128 bp (SSE register size)
Amending requires:
  4(2E+1) bitwise OR.
  4(2E+1) packed shuffle.
  3(2E+1) shift.
GateKeeper
SHD

## Slide 127: GateKeeper: Speed & Accuracy Results
90x-130x faster filter
than SHD (Xin et al., 2015) and the Adjacency Filter (Xin et al., 2013)
4x lower false accept rate
than the Adjacency Filter (Xin et al., 2013)
10x speedup in read mapping
with the addition of GateKeeper to the mrFAST mapper (Alkan et al., 2009)
Freely available online github.com/BilkentCompGen/GateKeeper

## Slide 128: GateKeeper Conclusions
FPGA-based pre-alignment greatly speeds up read mapping
  10x speedup of a state-of-the-art mapper (mrFAST)
FPGA-based pre-alignment can be integrated with the sequencer
  It can help to hide the complexity and details of the FPGA
  Enables real-time filtering while sequencing

## Slide 129: More on GateKeeper
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 130: MAGNET Accelerator [Alser+, TIR 2017]
Notes: We implement our algorithm in Verilog and design a hardware accelerator for it. Each processing core is able to examine a single mapping. We integrate many hardware processing cores in the architecture of MAGNET for examining many mappings in a parallel fashion.

## Slide 131: Can We Do Better?
Faster, More Accurate,
More Scalable
Pre-Alignment Filtering

## Slide 132: Algorithm-Arch-Device Co-Design is Critical
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (expanded view)

## Slide 133: Shouji (障子) [Alser+, Bioinformatics 2019]
Mohammed Alser, Hasan Hassan, Akash Kumar, Onur Mutlu, and Can Alkan, "Shouji: A Fast and Efficient Pre-Alignment Filter for Sequence Alignment" Bioinformatics, [published online, March 28], 2019. [Source Code] [Online link at Bioinformatics Journal]

## Slide 134: Shouji
Key observation:
  Correct alignment always includes long identical subsequences
  Processing the entire sequence at once is ineffective for hardware design
Key idea:
  Use an overlapping sliding window approach to quickly and accurately find all long identical subsequences (consecutive zeros)
Key result:
  Shouji accelerates the best-performing CPU read aligner Edlib (Bioinformatics 2017) by up to 18.8x using 16 filtering units that work in parallel
  Shouji on FPGA is up to 10,000x faster than on CPU
  Shouji is 2.4x to 467x more accurate than GateKeeper (Bioinformatics 2017) and SHD (Bioinformatics 2015)

## Slide 135: Shouji
Key observation:
  Correct alignment always includes long identical subsequences
Dot plot, dot matrix
(Lipman and Pearson, 1985)

## Slide 136
Shouji Walkthrough
1
1
1
4
1
2
1
0
0
0
0
Build the Neighborhood Map
Store longest subsequence
in Shouji Bit-vector
1
1
3
1
0
2
0
0
0
1
0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1
Find all common subsequences (diagonal segments of consecutive zeros) shared between two given sequences
ACCEPT iff number of ‘1’s ≤ Threshold
Shouji: a fast and efficient pre-alignment filter for sequence alignment, Bioinformatics 2019,
https://doi.org/10.1093/bioinformatics/btz234

## Slide 137: Effect of Sliding Window Size
Large enough window to accurately capture longer streaks of matches  lower false positives
Small enough window to perform fast computation
Chart: Window Size (bits)
| 1 | 2 | 3 | 4
FP | 0.52859 | 0.17299 | 0.036783 | 0.011039

## Slide 138: Hardware Implementation
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Counting is performed concurrently for all bit-vectors and
all sliding windows in a single clock cycle using multiple 4-input LUTs

## Slide 139: More on Shouji (障子) [Alser+, Bioinformatics 2019]
Mohammed Alser, Hasan Hassan, Akash Kumar, Onur Mutlu, and Can Alkan, "Shouji: A Fast and Efficient Pre-Alignment Filter for Sequence Alignment" Bioinformatics, [published online, March 28], 2019. [Source Code] [Online link at Bioinformatics Journal]

## Slide 140: SneakySnake [Alser+, Bioinformatics 2020]
Mohammed Alser, Taha Shahroodi, Juan-Gomez Luna, Can Alkan, and Onur Mutlu, "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs" Bioinformatics, to appear in 2020. [Source Code] [Online link at Bioinformatics Journal]

## Slide 141: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches
Dot plot, dot matrix
(Lipman and Pearson, 1985)

## Slide 142: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches
Key idea:
  Reduce the approximate string matching problem to the Single Net Routing problem in VLSI chip layout
VLSI chip layout

## Slide 143: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches
Key idea:
  Reduce the approximate string matching problem to the Single Net Routing problem in VLSI chip layout
Key result:
  SneakySnake is up to four orders of magnitude more accurate than Shouji (Bioinformatics’19) and GateKeeper (Bioinformatics’17)
  SneakySnake greatly accelerates state-of-the-art CPU sequence aligners, Edlib (Bioinformatics’17) and Parasail (BMC Bioinformatics’16)
    by up to 37.7× and 43.9× (>12× on average), on CPUs
    by up to 413× and 689× (>400× on average) with FPGAs/GPUs

## Slide 144: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
E = 3
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 145: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
E = 3
ENTRANCE
EXIT
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 146: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
3
EXIT
2
1
0
0
0
4
0
2
0
0
ENTRANCE
0
0
0
4
1
0
1
0
1
1
0
1
0
0
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 147: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Routing Travel Path
Examining the Snake Survival
This is what you actually need to build and it can be done on-the-fly!
ENTRANCE
EXIT
3
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 148: FPGA Resource Analysis
FPGA resource usage for a single filtering unit of GateKeeper, Shouji, and Snake-on-Chip for a sequence length of 100 and under different edit distance thresholds (E).

## Slide 149: Key Results of SneakySnake
  SneakySnake is up to four orders of magnitude more accurate than Shouji (Bioinformatics’19) and GateKeeper (Bioinformatics’17)
  Short reads:
    SneakySnake accelerates Edlib (Bioinformatics’17) and Parasail (BMC Bioinformatics’16) by
    up to 37.7× and 43.9× (>12× on average), on CPUs
    up to 413× and 689× (>400× on average) using FPGAs/GPUs
  Long reads:
    SneakySnake accelerates Parasail and KSW2 by 140.1× and 17.1× on average, respectively, on CPUs

## Slide 150: Long Read Mapping (SneakySnake vs Parasail)
10K bp reads 100K bp reads

## Slide 151: Long Read Mapping (SneakySnake vs KSW2)
10K bp reads 100K bp reads

## Slide 152: More on SneakySnake [Alser+, Bioinformatics 2020]
Mohammed Alser, Taha Shahroodi, Juan-Gomez Luna, Can Alkan, and Onur Mutlu, "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs" Bioinformatics, to appear in 2020. [Source Code] [Online link at Bioinformatics Journal]

## Slide 153: GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 154: Problem & Our Goal
Multiple steps of read mapping require approximate string matching
  ASM enables read mapping to account for sequencing errors and genetic variations in the reads
ASM makes up a significant portion of read mapping (more than 70%)
One of the major bottlenecks of genome sequence analysis
Our Goal:
Accelerate approximate string matching by designing a fast and flexible framework,
which can be used to accelerate multiple steps of the genome sequence analysis pipeline
Notes: As a result, read mapping must perform approximate string matching (ASM). Several algorithms exist for ASM, but state-of-the-art read mapping tools typically make use of an expensive dynamic programming based algorithm that scales quadratically in both execution time and required storage. This ASM algorithm is the major bottleneck for many steps of the genome sequence analysis pipeline.
Thus, our goal in this work is to design a fast and flexible framework for both short and long reads, which can be used to accelerate multiple steps of the genome sequence analysis pipeline.

## Slide 155: GenASM: ASM Framework for GSA
GenASM: First ASM acceleration framework for GSA
  Based on the Bitap algorithm
    Uses fast and simple bitwise operations to perform ASM
  Modified and extended ASM algorithm
    Highly-parallel Bitap with long read support
    Bitvector-based novel algorithm to perform traceback
  Co-design of our modified scalable and memory-efficient algorithms with low-power and area-efficient hardware accelerators
Our Goal:
Accelerate approximate string matching
by designing a fast and flexible framework,
which can accelerate multiple steps of genome sequence analysis
Notes: [CLICK] Our goal in this work is to design a fast and flexible framework for both short and long reads, which can accelerate multiple steps of genome sequence analysis (GSA).
[CLICK] To this end, we propose GenASM
[CLICK] We base GenASM on Bitap, an ASM algorithm that uses only fast and simple bitwise operations, making it amenable to efficient hardware acceleration. To our knowledge, GenASM is the first work that enhances and accelerates Bitap, and also it is the first ASM acceleration framework for genome sequence analysis.
[CLICK] We modify Bitap to support long reads and to enable parallelization.
We also develop a novel Bitap-compatible algorithm for traceback, which uses information collected during ASM about the different types of errors to identify the optimal alignment of reads.
[CLICK] And, we co-design specialized, low-power and area-efficient hardware for both algorithms.

## Slide 156: GenASM: Hardware Design
GenASM-DC
GenASM-TB
GenASM-DC:
generates bitvectors
and performs edit
Distance Calculation
GenASM-TB: performs TraceBack and assembles the optimal alignment
Host CPU
TB-SRAM1
TB-SRAM2
TB-SRAMn
GenASM-TB
Accelerator
GenASM-DC
Accelerator
GenASM-TB
Accelerator
GenASM-DC
Accelerator
Main Memory
DC-SRAM
DC-SRAM
GenASM-DC
GenASM-TB
TB-SRAM1
TB-SRAM2
TB-SRAMn
.
.
.
Notes: Our co-designed hardware consists of two components:
(1) GenASM-DC, which provides hardware support to efficiently execute our modified Bitap algorithm to perform distance calculation; and
(2) GenASM-TB, which provides hardware support to efficiently execute our novel traceback algorithm to find the optimal alignment.
GenASM also has two types of SRAM buffers:
DC-SRAM, and
TB-SRAMs

## Slide 157: GenASM: Hardware Design
GenASM-DC
GenASM-TB
GenASM-DC:
generates bitvectors
and performs edit
Distance Calculation
GenASM-TB: performs TraceBack and assembles the optimal alignment
Host CPU
TB-SRAM1
TB-SRAM2
TB-SRAMn
GenASM-TB
Accelerator
GenASM-DC
Accelerator
GenASM-TB
Accelerator
GenASM-DC
Accelerator
Main Memory
DC-SRAM
DC-SRAM
GenASM-DC
GenASM-TB
TB-SRAM1
TB-SRAM2
TB-SRAMn
.
.
.
Our specialized compute units and on-chip SRAMs help us to:
Match the rate of computation with memory capacity and bandwidth
Achieve high performance and power efficiency
Scale linearly in performance with the number of parallel compute units that we add to the system
Notes: Our specialized compute units and on-chip SRAMs help us to:
[CLICK] (1) Match the rate of computation with memory capacity and bandwidth
[CLICK] (2) Achieve high performance and power efficiency
[CLICK] (3) Scale linearly in performance with the number of parallel compute units that we add to the system

## Slide 158: GenASM-DC: Hardware Design
Linear cyclic systolic array based accelerator
  Designed to maximize parallelism and minimize memory bandwidth and memory footprint
Processing Block (PB)
Processing Core (PC)
Notes: [CLICK] We implement GenASM-DC as a linear cyclic systolic array based accelerator, using small and very simple logic components.
[CLICK] This design helps us to maximize parallelism and minimize memory BW and footprint.
[CLICK] Processing Core is the basic compute component which computes the intermediate bitvectors
[CLICK] and when we add the flip-flop-based storage logic around Processing Core, we define a Processing Element (PE)
[CLICK] Multiple PEs are concatenated to define a Processing Block
[CLICK] We also have DC-SRAM, which stores the reference text, the pattern bitmasks for the query read, and the intermediate data generated from PEs, and we also have
[CLICK] TB-SRAMs, which store the intermediate bitvectors generated by each PE of GenASM-DC for later use by GenASM-TB.

## Slide 159: GenASM-TB: Hardware Design
Bitwise Comparisons
CIGAR string
Last CIGAR
<<
match
CIGAR
out
1
2
.
.
64
192
insertion
deletion
subs
64
64
64
64
1
2
Next Rd Addr Compute
3
GenASM-TB
Very simple logic:
  ❶Reads the bitvectors from one of the TB-SRAMs using the computed address
  ❷Performs the required bitwise comparisons to find the traceback output for the current position
  ❸Computes the next TB-SRAM address to read the new set of bitvectors
Bitwise Comparisons
CIGAR string
Last CIGAR
<<
match
CIGAR
out
1
2
.
.
64
192
insertion
deletion
subs
64
64
64
64
to main
memory
1
2
Next Rd Addr Compute
3
1.5KB
TB-SRAM1
1.5KB
TB-SRAM2
1.5KB
TB-SRAM64
1
2
3
Notes: [CLICK] We implement GenASM-TB hardware using very simple logic, which
[CLICK] 1) reads the bitvectors from one of the TB-SRAMs using the computed address,
[CLICK] 2) performs the required bitwise comparisons to find the traceback output for the current position, and
[CLICK] 3) computes the next TB-SRAM address to read the new set of bitvectors.
After GenASM-TB finds the complete traceback output, [CLICK] it writes this output to main memory and completes its execution.

## Slide 160: Key Results – Area and Power
Based on our synthesis of GenASM-DC and GenASM-TB accelerator datapaths using the Synopsys Design Compiler with a 28nm LP process:
  Both GenASM-DC and GenASM-TB operate @ 1GHz
  Total (1 vault): 0.334 mm2 0.101 W
  Total (32 vaults): 10.69 mm2 3.23 W
  % of a Xeon CPU core: 1% 1%
Notes: [CLICK] We synthesize our DC and TB accelerator datapaths with a typical 28nm low-power process:
[CLICK] Both accelerators operates at 1GHz.
[CLICK] We find that for 32 GenASM accelerator (one for each HMC vault), total area overhead is ten point sixty nine millimeter square and total power consumption is three point twenty-three watts.
We observe that both area and power consumption of GenASM (at 1 vault) is around 1% of the area and power consumption of a single Xeon CPU core.

## Slide 161: Key Results – Area and Power
Based on our synthesis of GenASM-DC and GenASM-TB accelerator datapaths using the Synopsys Design Compiler with a 28nm LP process:
  Both GenASM-DC and GenASM-TB operate @ 1GHz
  GenASM has low area and power overheads
Notes: Thus, GenASM has low area and power overheads.

## Slide 162: Use Cases of GenASM
Indexing
Seeding
Pre-Alignment Filtering
Read Alignment
Reference genome
Hash table based index
Candidate mapping locations
Optimal alignment
Reads from sequenced genome
Remaining candidate mapping locations
Indexing
Seeding
Notes: GenASM is flexible and can be used for a number of use cases.
In this work, we evaluate three of them in detail and two of them are from the read mapping pipeline:
Pre-alignment filtering and read alignment

## Slide 163: Use Cases of GenASM (cont’d.)
Read Alignment Step of Read Mapping
  Find the optimal alignment of how reads map to candidate reference regions
Pre-Alignment Filtering for Short Reads
  Quickly identify and filter out the unlikely candidate reference regions for each read
Edit Distance Calculation
  Measure the similarity or distance between two sequences
We also discuss other possible use cases of GenASM in our paper:
  Read-to-read overlap finding, hash-table based indexing, whole genome alignment, generic text search
Notes: [CLICK] (1) read alignment
is the most time consuming step of read mapping that we align each read to all of its candidate reference regions and then find the optimal alignment.
[CLICK] (2) in pre-alignment filtering for short reads,
we aim to quickly identify and filter out the unlikely candidate reference regions of each read by approximating the edit distance between them and filter out if it is above a threshold.
[CLICK] And our third use case is edit distance calculation
Which is one of the fundamental operations in genomics that measures the similarity or distance btw two sequences
In our paper, we also briefly discuss several other use cases such as generic text search

## Slide 164: Key Results
Read Alignment
116× speedup, 37× less power than Minimap2 (state-of-the-art SW)
111× speedup, 33× less power than BWA-MEM (state-of-the-art SW)
3.9× better throughput, 2.7× less power than Darwin (state-of-the-art HW)
1.9× better throughput, 82% less logic power than GenAx (state-of-the-art HW)
Pre-Alignment Filtering
3.7× speedup, 1.7× less power than Shouji (state-of-the-art HW)
Edit Distance Calculation
22–12501× speedup, 548–582× less power than Edlib (state-of-the-art SW)
9.3–400× speedup, 67× less power than ASAP (state-of-the-art HW)
Notes: We find that, for all the three use cases, GenASM is significantly more efficient in terms of both speed and power consumption than state-of-the-art software and hardware baselines

## Slide 165: More on GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 166: Accelerating Sequence-to-Graph Mapping
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 167: Genome Sequence Analysis
Sequence-to-sequence mapping (traditional read mapping):
  Critical step in genome sequence analysis (GSA)
  Maps reads collected from an individual to a known linear reference genome sequence
  Well studied with many available tools and accelerators
Recent works replace the linear reference sequence with a graph-based representation of the reference genome (genome graph)
  Captures the genetic variations and diversity across many individuals in a population
Sequence-to-graph mapping results in notable quality improvements in GSA
  More difficult computational problem
  Much smaller number of practical software tools currently available
  No prior hardware design for graph-based GSA
Notes: [CLICK] A critical step of genome sequence analysis is the mapping of sequenced DNA fragments (i.e., reads) collected from an individual to a known linear reference genome sequence (i.e., sequence-to-sequence mapping).
[CLICK] Recent works replace the linear reference sequence with a graph-based representation of the reference genome, which captures the genetic variations and diversity across many individuals in a population.
[CLICK] Mapping reads to the graph-based reference genome (i.e., sequence-to-graph mapping) results in notable quality improvements in genome analysis. Unfortunately, while sequence-to-sequence mapping is well studied with many available tools and accelerators, sequence-to-graph mapping is a more difficult computational problem, with a much smaller number of practical software tools currently available.

## Slide 168: SeGraM: First Graph Mapping Accelerator
SeGraM: First universal genomic mapping accelerator
MinSeed: The first minimizer-based seeding accelerator
BitAlign: The first (bitvector-based) sequence-to-graph alignment accelerator
Our Goal:
Specialized, high-performance, scalable, and low-cost algorithm/hardware co-design that alleviates bottlenecks in both the seeding and alignment steps of
sequence-to-graph mapping
Design an accelerator that is efficient for both
linear and graph-based read mapping
Notes: [CLICK] Based on our analysis with two state-of-the-art sequence-to-graph mapping tools, we reveal four key issues and find that there is a pressing need to have a specialized, high-performance, scalable, and low-cost algorithm/hardware co-design that alleviates bottlenecks in both the seeding and alignment steps of sequence-to-graph mapping.
[CLICK] Since sequence-to-sequence mapping can be treated as a special case of sequence-to-graph mapping, we aim to design an accelerator that is efficient for both linear and graph-based read mapping.
[CLICK] To this end, we propose SeGraM, a universal algorithm/hardware co-designed genomic mapping accelerator that can effectively and efficiently support both sequence-to-graph mapping and sequence-to-sequence mapping, for both short and long reads. To our knowledge, SeGraM is the first algorithm/hardware co-design for accelerating
sequence-to-graph mapping.
[CLICK] SeGraM consists of two main components: (1) MinSeed, the first minimizer-based seeding accelerator, which finds the candidate locations in a given genome graph; and
[CLICK] (2) BitAlign, the first bitvector-based sequence-to-graph alignment accelerator, which performs alignment between a given read and the subgraph identified by MinSeed.

## Slide 169: Use Cases & Key Results
Sequence-to-Graph (S2G) Mapping
5.9×/106× speedup, 4.1×/3.0× less power than GraphAligner for long and short reads, respectively (state-of-the-art SW)
3.9×/742× speedup, 4.4×/3.2× less power than vg for long and short reads, respectively (state-of-the-art SW)
Sequence-to-Graph (S2G) Alignment
41×–539× speedup over PaSGAL with AVX-512 support (state-of-the-art SW)
Sequence-to-Sequence (S2S) Alignment
1.2×/4.8× higher throughput than GenASM and GACT of Darwin for long reads (state-of-the-art HW)
1.3×/2.4× higher throughput than GenASM and SillaX of GenAX for short reads (state-of-the-art HW)
Notes: [CLICK] We demonstrate that SeGraM provides significant improvements for multiple steps of the sequence-to-graph (i.e., S2G) and sequence-to-sequence (i.e., S2S) mapping pipelines.
[CLICK] We show that (1) SeGraM provides greatly higher throughput and lower power consumption on both short and long reads compared to state-of-the-art software tools for sequence-to-graph mapping, and
[CLICK] (2) BitAlign significantly outperforms a state-of-the-art sequence-to-graph alignment tool and [CLICK] three state-of-the-art hardware solutions that are specifically designed for sequence-to-sequence alignment.
===========================================================================================================
We also show that MinSeed can be employed for the seeding step of both sequence-to-graph and sequence-to-sequence mapping pipelines.

## Slide 170: Accelerating Sequence-to-Graph Mapping
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 171: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 172: Read Mapping & Filtering
Problem: Heavily bottlenecked by Data Movement
GateKeeper, Shouji, SneakySnake performance limited by DRAM bandwidth [Alser+, Bioinformatics 2017,2019,2020]
Ditto for SHD [Xin+, Bioinformatics 2015]
Solution: Processing-in-memory can alleviate the bottleneck
We need to design mapping & filtering algorithms to fit processing-in-memory

## Slide 173: Read Mapping & Filtering in Memory
We need to design
mapping & filtering algorithms
that fit processing-in-memory

## Slide 174: Near-Memory Pre-Alignment Filtering
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]

## Slide 175: Near-Memory SneakySnake
Problem: Read mapping is heavily bottlenecked by data movement from main memory
Solution: Perform read mapping near where data resides using specialized logic
We carefully redesign the accelerator logic of SneakySnake to exploit near-memory computation capability on real FPGA boards that use HBM (high-bandwidth memory)
Near-memory SneakySnake improves performance and energy efficiency by 27.4× and 133×, respectively, over a 16-core (64-thread) IBM POWER9 CPU

## Slide 176: Near-Memory Acceleration using FPGAs
IBM POWER9 CPU
HBM-based FPGA board
OCAPI
Source: AlphaData
Source: IBM
Near-HBM FPGA-based accelerator
Two communication technologies: CAPI2 and OCAPI
Two memory technologies: DDR4 and HBM
Two workloads: Weather Modeling and Genome Analysis
Notes: To this end we build a [CLICK] near-HBM FPGA based accelerator which is connected to a server-grade IBM POWER9-based CPU system

## Slide 177: Performance & Energy Greatly Improve
5-27× performance vs. a 16-core (64-thread) IBM POWER9 CPU
HBM alleviates memory bandwidth contention vs. DDR4
12-133× energy efficiency vs. a 16-core (64-thread) IBM POWER9 CPU
Notes: [CLICK]

## Slide 178: More On Near-Memory SneakySnake
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]

## Slide 179: Location Filtering in 3D-Stacked PIM
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" BMC Genomics, 2018. Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. [Slides (pptx) (pdf)] [Source Code] [arxiv.org Version (pdf)] [Talk Video at AACBB 2019]

## Slide 180: GRIM-Filter
Key observation: FPGA and GPU accelerators are heavily bottlenecked by data movement
Key idea: exploit the high memory bandwidth and the logic layer of 3D-stacked memory to perform highly-parallel filtering in the DRAM chip itself
GRIM-Filter, an algorithm-hardware co-designed PIM system for pre-alignment filtering
Key results:
  GRIM-Filter is 1.8x-3.7x (2.1x on average) faster than the FastHASH filter (BMC Genomics’13) across real data sets
  GRIM-Filter has 5.6x-6.4x (6.0x on average) lower false accept rate than the FastHASH filter (BMC Genomics’13) across real data sets

## Slide 181: Our Proposal: GRIM-Filter
Data Structures: Bins & Bitvectors
Checking a Bin
Integrating GRIM-Filter into a Mapper

## Slide 182: GRIM-Filter: Bins
We partition the genome into large sequences (bins).
… GGAAATACGTTCAGTCAGTTGGAAATACGTTTTGGGCGTTACTTCTCAGTACGTACAGTACAGTAAAAATGACAGTAAGAC …
Bin x - 3
Bin x - 2
Bin x - 1
Bin x
1
0
1
…
1
0
0
…
1
Bitvector
AAAAA
AAAAC
AAAAT
…
CCCCC
CCCCT
CCCCG
…
GGGGG
AAAAA exists in bin x
CCCCT doesn’t exist in bin x
  Represent each bin with a bitvector that holds the occurrence of all permutations of a small string (token) in the bin
  To account for matches that straddle bins, we employ overlapping bins
    A read will now always completely fall within a single bin
Notes: [CLICK]
We first partition the genome in large sequences that we refer to as bins
[CLICK]
[CLICK]
We show the genome with an arbitrary bin highlighted
[CLICK]
We then generate a bitvector that represents the bin and holds the occurrence of all permutations of a small string called a token in the bin
we see in the figure that tokens that exist in the bin are represented with a 1, and those not in the bin are a 0.
[CLICK]
so AAAAA exists in Bin x
and CCCCT does not exist in bin x
[CLICK]
to account for matches straddling two bins, we employ overlapping bins so that a read will now always fall within a single bin
[END-CLICK]

## Slide 183: GRIM-Filter: Bitvectors
  Reasonable memory footprint to hold pre-computed vectors which are generated per bin
    Only simple add/compare operations on vectors for likelihood
  At the cost of
    Lower approximate string matching accuracy
    Becoming a memory-bound process
… C G T G A G T C …
Bin x
0
…
…
…
…
…
Bin x Bitvector
AAAAA
…
CGTGA
…
TGAGT
…
GAGTC
…
GTGAG
…
C G T G A
G T G A G
T G A G T
G A G T C
1
0
0
0
0
1
1
1

## Slide 184: GRIM-Filter: Bitvectors
Storing all bitvectors
requires bits
in memory,
where t = number of bins.
For bin size ~200, and n = 5,
memory footprint
~3.8 GB
AAAAA
AAAAC
AAAAG
AAAAT
.
CCCCT
.
.
.
.
GCATG
.
TTGCA
.
TTTTT
1
1
0
0
.
1
.
.
.
.
1
.
1
.
0
0
1
0
.
1
.
1
.
1
.
1
.
.
.
0
AAAAA
AAAAC
AAAAG
.
AGAAA
.
GAAAA
.
GACAG
.
GCATG
.
.
.
TTTTT
  
b1
b2
tokens
Notes: We use bitvectors to quickly figure out existence within a bin
We see here a list of bit vectors that are associated with a particular bin. The memory required to store all bit vectors is found by multiplying the number of bins by 4^q bits (which is the size of the bit vectors)
For a bin size of 200 and a q of 5, the memory footprint comes to around 3.8 GB
[END-CLICK]

## Slide 185: Our Proposal: GRIM-Filter
Data Structures: Bins & Bitvectors
Checking a Bin
Integrating GRIM-Filter into a Mapper

## Slide 186: GRIM-Filter: Checking a Bin
TTGGA
GAACT
AACTT
ACTTG
CTTGG
INPUT: Read Sequence r
GAACTTGGAGTCTA CGAG
...
Read bitvector for bin_num(x)
...
1
+
≥ Threshold?
Send to
Read Mapper for Sequence Alignment
tokens
Discard
NO
YES
Sum
How GRIM-Filter determines whether to discard potential match locations in a given bin prior to alignment
3
2
4
5
1
0
1
0
1
1
1
0
0
.
.
.
.
.
.
Get tokens
Match tokens to bitvector
Compare
Notes: Talk about why GRIM-Filter is faster than alignment. This is obviously faster than dynamic programming.
This threshold value changes error tolerance
In this example, we will use a token size of 5
We show how GRIM-Filter determines the need for alignment in a bin X. We use the read to generate a mask to selectively sum bit vectors.
[CLICK]
For the given read sequence in red, we find all indices corresponding to the q-grams found in the read.
[CLICK]
We then query and [CLICK] sum the bits of bin X’s pre-computed bit vector of the reference genome.
This final value is then compared to a threshold to determine the likelihood of this read’s existence in Bin X
These are all very simple operations and can be run in parallel across different bins
[END-CLICK]

## Slide 187: Our Proposal: GRIM-Filter
Data Structures: Bins & Bitvectors
Checking a Bin
Integrating GRIM-Filter into a Mapper

## Slide 188: Integrating GRIM-Filter into a Read Mapper
GRIM-Filter: Seed Location Checker
0001010 011010
...
...
...
GAACTTGCGAG GTATT
...
INPUT: Read Sequence
GRIM-Filter:
Filter Bitmask Generator
Seed Location Filter Bitmask
0001010 011010
...
...
...
020128
020131
414415
...
...
...
...
KEEP
x
DISCARD
KEEP
INPUT: All Potential Seed Locations
Read Mapper: Sequence Alignment
Reference Segment Storage
Edit-Distance Calculation
reference segment @ 020131
reference segment @ 414415
. . .
OUTPUT: Correct Mappings
1
2
4
3
Notes: REWRITE
In this example, we will use a token size of 5
We show how GRIM-Filter determines the need for alignment in a bin X. We use the read to generate a mask to selectively sum bit vectors.
[CLICK]
For the given read sequence in red, we find all indices corresponding to the q-grams found in the read.
[CLICK]
We then query and [CLICK] sum the bits of bin X’s pre-computed bit vector of the reference genome.
This final value is then compared to a threshold to determine the likelihood of this read’s existence in Bin X
These are all very simple operations and can be run in parallel across different bins
[END-CLICK]

## Slide 189: Key Properties of GRIM-Filter
Simple Operations:
  To check a given bin, find the sum of all bits corresponding to each token in the read
  Compare against threshold to determine whether to align
Highly Parallel: Each bin is operated on independently and there are many many bins
Memory Bound: Given the frequent accesses to the large bitvectors, we find that GRIM-Filter is memory bound
These properties together make GRIM-Filter a good algorithm to be run in 3D-Stacked DRAM
Notes: As a recap,
[CLICK]
GRIM-Filter is comprised of very simple addition/comparison operations
[CLICK]
To check a given bin, we sum the bits corresponding to each token in the read
[CLICK]
and then we compare the sum against a threshold to determine whether we need to align
[CLICK]
It is also highly parallel
each bin is operated on independently and there are many many bins
[CLICK]
These three properties together make it a suitable algorithm to be run in 3D stacked DRAM
[END-CLICK]

## Slide 190: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 191: DRAM Landscape (circa 2015)
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.

## Slide 192: 3D-Stacked Memory
3D-Stacked DRAM architecture has extremely high bandwidth as well as a stacked customizable logic layer
  Logic Layer enables Processing-in-Memory, via high-bandwidth low-latency access to DRAM layers
  Embed GRIM-Filter operations into DRAM logic layer and appropriately distribute bitvectors throughout memory
Memory Array
Customized Logic
DRAM Layers
Logic Layer
TSVs
Notes: THICKEN TSV lines
[CLICK]
3D stacked memory stacks a logic layer and DRAM layers with vertical connections called TSVs. This vertical structure allows for a much higher number of connections increasing the available bandwidth. The customizable logic layer enables processing-in-memory, which avoids overloading the memory bus by offloading computation to this layer in the 3D stacked module.
We can design the simple operations required for GRIM-Filter into the customizable logic layer and appropriately distribute the bitvectors to enable an efficient filter
[CLICK]
Real 3D-stacked DRAM technologies are commercially available now such as high bandwidth memory
[CLICK]
And micron’s hybrid memory cube, among others
[END-CLICK]

## Slide 193: 3D-Stacked Memory
3D-Stacked DRAM architecture has extremely high bandwidth as well as a stacked customizable logic layer
  Logic Layer enables Processing in Memory, offloading computation to this layer and alleviating the memory bus
  Embed GRIM-Filter operations into DRAM logic layer and appropriately distribute bitvectors throughout memory
Memory Array
Customized Logic
http://i1-news.softpedia-static.com/images/news2/Micron-and-Samsung-Join-Force-to-Create-Next-Gen-Hybrid-Memory-2.png
Notes: [CLICK]
3D stacked memory stacks a logic layer and DRAM layers with vertical connections called TSVs. This vertical structure allows for a much higher number of connections increasing the available bandwidth. The customizable logic layer allows for processing-in-memory, which avoids overloading the memory bus by offloading computation to this layer in the 3D stacked module.
We can design the simple operations required for GRIM-Filter into the customizable logic layer and appropriately distribute the bit vectors to enable an efficient filter
[CLICK]
Real 3D-stacked DRAM technologies are commercially available now such as high bandwidth memory
[CLICK]
And micron’s hybrid memory cube, among others
[END-CLICK]

## Slide 194: 3D-Stacked Memory
3D-stacked DRAM architecture has extremely high bandwidth as well as a stacked customizable logic layer
  Logic Layer enables Processing in Memory, offloading computation to this layer and alleviating the memory bus
  Embed GRIM-Filter operations into DRAM logic layer and appropriately distribute bitvectors throughout memory
Memory Array
Customized Logic
http://i1-news.softpedia-static.com/images/news2/Micron-and-Samsung-Join-Force-to-Create-Next-Gen-Hybrid-Memory-2.png
http://images.anandtech.com/doci/9266/HBMCar_678x452.jpg
Notes: [CLICK]
3D stacked memory stacks a logic layer and DRAM layers with vertical connections called TSVs. This vertical structure allows for a much higher number of connections increasing the available bandwidth. The customizable logic layer allows for processing-in-memory, which avoids overloading the memory bus by offloading computation to this layer in the 3D stacked module.
We can design the simple operations required for GRIM-Filter into the customizable logic layer and appropriately distribute the bit vectors to enable an efficient filter
[CLICK]
Real 3D-stacked DRAM technologies are commercially available now such as high bandwidth memory
[CLICK]
And micron’s hybrid memory cube, among others
[END-CLICK]

## Slide 195: GRIM-Filter in 3D-Stacked DRAM
Each DRAM layer is organized as an array of banks
  A bank is an array of cells with a row buffer to transfer data
The layout of bitvectors in a bank enables filtering many bins in parallel
Notes: [CLICK]
Each DRAM layer is organized as an array of Banks
[CLICK]
and a bank is an array of cells with a row buffer. The row buffer holds one row at a time and uses this structure to transfer data with high bandwidth into the logic layer via TSVs
[CLICK]
We now show the distribution of bit vectors across the DRAM arrays to enable parallel processing of many bins.
[CLICK]
Each row represents a token's occurrence across many sequential bins. and the row of the appropriate token gets queried to find a vector showing the occurrence of the token across many bins.
These are the vectors are brought down into the logic layer to be operated on.
[CLICK]
[END-CLICK]

## Slide 196: GRIM-Filter in 3D-Stacked DRAM
Customized logic for accumulation and comparison per genome segment
  Low area overhead, simple implementation
  For HBM2, we use 4096 incrementer LUTs, 7-bit counters, and comparators in logic layer
Details are in [Kim+, BMC Genomics 2018]
Notes: [CLICK]
We now look at the implementation of logic in the logic layer
[CLICK]
GRIM-Filter only requires a very simple design for enabling the bitvector sum and threshold compare across many bins simultaneously. One comparator, incrementer, accumulator, and buffer for each bin that we are checking in parallel
[CLICK]
This results in a very low area overhead and ease of implementation
[END-CLICK]

## Slide 197: Methodology
Performance simulated using an in-house 3D-Stacked DRAM simulator
Evaluate 10 real read data sets (From the 1000 Genomes Project)
  Each data set consists of 4 million reads of length 100
Evaluate two key metrics
  Performance
  False negative rate
    The fraction of locations that pass the filter but result in a mismatch
  Compare against a state-of-the-art filter, FastHASH [Xin+, BMC Genomics 2013] when using mrFAST, but GRIM-Filter can be used with ANY read mapper

## Slide 198: GRIM-Filter Performance
2.1x average performance benefit
1.8x-3.7x performance benefit across real data sets
Chart: 
| ERR240726-1 | ERR240726-2 | ERR240727-1 | ERR240727-2 | ERR240728-1 | ERR240728-2 | ERR240729-1 | ERR240729-2 | ERR240730-1 | ERR240730-2 | Average
FastHASH | 37.7881 | 47.2858 | 26.4744 | 29.611 | 26.3053 | 28.5216 | 26.3319 | 27.6094 | 63.5181 | 27.748 | 34.1194
GRIM-3D | 15.2292 | 19.6862 | 14.5846 | 17.6976 | 14.573 | 17.0455 | 14.6994 | 15.4576 | 17.3955 | 15.7755 | 16.2144
e = 0.05
Sequence Alignment Error Tolerance (e)
Time (×1000 seconds)
FastHASH filter
GRIM-Filter
Benchmarks and their Execution Times
GRIM-Filter gets performance due to its hardware-software co-design
Notes: We ran 10 separate experiments with real read data sets, consisting of approximately 4 million reads each, and got the following results. Compared to the previous best filter, our filter enjoys a 2x average end-to-end read mapper performance gain across the data sets, and a 6x average lower false negative rate. Again, these are the locations that were not discarded by the filter, but were then later discarded after alignment

## Slide 199: GRIM-Filter False Negative Rate
6.0x average reduction in False Negative Rate
5.6x-6.4x False Negative reduction across real data sets
False Negative Rate
e = 0.05
FastHASH filter
GRIM-Filter
Chart: 
| ERR240726-1 | ERR240726-2 | ERR240727-1 | ERR240727-2 | ERR240728-1 | ERR240728-2 | ERR240729-1 | ERR240729-2 | ERR240730-1 | ERR240730-2 | Average
FastHASH | 0.40191 | 0.38648 | 0.40237 | 0.38943 | 0.40263 | 0.38846 | 0.40149 | 0.3892 | 0.40136 | 0.38925 | 0.39526
GRIM-3D | 0.066592 | 0.067988 | 0.063272 | 0.067891 | 0.064197 | 0.069488 | 0.066264 | 0.066911 | 0.062599 | 0.067789 | 0.066299
Benchmarks and their False Negative Rates
Sequence Alignment Error Tolerance (e)
GRIM-Filter utilizes more information available in the read to filter
Notes: We ran 10 separate experiments with real read data sets, consisting of approximately 4 million reads each, and got the following results. Compared to the previous best filter, our filter enjoys a 2x average end-to-end read mapper performance gain across the data sets, and a 6x average lower false negative rate. Again, these are the locations that were not discarded by the filter, but were then later discarded after alignment

## Slide 200: More on GRIM-Filter
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" BMC Genomics, 2018. Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. [Slides (pptx) (pdf)] [Source Code] [arxiv.org Version (pdf)] [Talk Video at AACBB 2019]

## Slide 201: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 202: In-Storage Genome Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 203: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement from Storage
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 204: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 205: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 206: Filtering Opportunities
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate and short
  Long reads: less accurate and long
High sequencing error rates (long reads) or
High genetic variation (short or long reads)
Non-matching reads
Do not have potential matching locations, so they skip alignment
Low sequencing error rates (short reads) combined with
Low genetic variation
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Reads that do not require the expensive alignment step:
Notes: Let’s take a look at filtering opportunities based on the input reads.
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate (99.9%) and short (e.g., up to a few hundreds of DNA characters)
  Long reads: less accurate (85-90%) and long (e.g., from hundreds to millions of DNA characters)
Based on these, We leverage two filtering opportunities
First, we can filter exactly matching reads, which are reads that match exactly to one or more subsequences of the reference genome and do not require approximate string matching during alignment. Exact matches can frequently occur in short read sets with low sequencing errors and low genetic variations
Second, we can filter non-matching reads. Such reads do not have any potential matching locations in the reference genome can skip the expensive alignment step. Non-matching reads can frequently occur in long read sets with high sequencing errors and short or long read sets with high genetic variations

## Slide 207: Challenges
Read mapping workloads can exhibit different behavior
There are limited hardware resources
in the storage system
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD. By addressing these challenges [CLICK]

## Slide 208: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 209: In-Storage Genome Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 210: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 211: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 212: More on Processing-in-Memory
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 213: A Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=H3sEaINPBOE

## Slide 214: Processing-in-Memory Landscape Today
[UPMEM 2019]
[Samsung 2021]
[SK Hynix 2022]
[Samsung 2021]
This does not include many experimental chips and startups
[Alibaba 2022]

## Slide 215: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 216: UPMEM Memory Modules
E19: 8 chips DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 217: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 218: More on the UPMEM PIM System
https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=26

## Slide 219: Experimental Analysis of the UPMEM PIM Engine
https://arxiv.org/pdf/2105.03814.pdf

## Slide 220: UPMEM PIM System Summary & Analysis
Juan Gomez-Luna, Izzat El Hajj, Ivan Fernandez, Christina Giannoula, Geraldo F. Oliveira, and Onur Mutlu, "Benchmarking Memory-Centric Computing Systems: Analysis of Real Processing-in-Memory Hardware" Invited Paper at Workshop on Computing with Unconventional Technologies (CUT), Virtual, October 2021. [arXiv version] [PrIM Benchmarks Source Code] [Slides (pptx) (pdf)] [Talk Video (37 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 221: PrIM Benchmarks: Application Domains
Domain | Benchmark | Short name
Dense linear algebra | Vector Addition | VA
 | Matrix-Vector Multiply | GEMV
Sparse linear algebra | Sparse Matrix-Vector Multiply | SpMV
Databases | Select | SEL
 | Unique | UNI
Data analytics | Binary Search | BS
 | Time Series Analysis | TS
Graph processing | Breadth-First Search | BFS
Neural networks | Multilayer Perceptron | MLP
Bioinformatics | Needleman-Wunsch | NW
Image processing | Image histogram (short) | HST-S
 | Image histogram (large) | HST-L
Parallel primitives | Reduction | RED
 | Prefix sum (scan-scan-add) | SCAN-SSA
 | Prefix sum (reduce-scan-scan) | SCAN-RSS
 | Matrix transposition | TRNS

## Slide 222: PrIM Benchmarks are Open Source
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 223: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 224: Understanding a Modern PIM Architecture
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 225: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 226: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=Pp9jSU2b9oM&list=PL5Q2soXY2Zi8_VVChACnON4sfh2bJ5IrD&index=159

## Slide 227: More on PRIM Benchmarks
Juan Gomez-Luna, Izzat El Hajj, Ivan Fernandez, Christina Giannoula, Geraldo F. Oliveira, and Onur Mutlu, "Benchmarking a New Paradigm: An Experimental Analysis of a Real Processing-in-Memory Architecture" Preprint in arXiv, 9 May 2021. [arXiv preprint] [PrIM Benchmarks Source Code] [Slides (pptx) (pdf)] [Long Talk Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [SAFARI Live Seminar Slides (pptx) (pdf)] [SAFARI Live Seminar Video (2 hrs 57 mins)] [Lightning Talk Video (3 minutes)]

## Slide 228: UPMEM PIM System Summary & Analysis
Juan Gomez-Luna, Izzat El Hajj, Ivan Fernandez, Christina Giannoula, Geraldo F. Oliveira, and Onur Mutlu, "Benchmarking Memory-Centric Computing Systems: Analysis of Real Processing-in-Memory Hardware" Invited Paper at Workshop on Computing with Unconventional Technologies (CUT), Virtual, October 2021. [arXiv version] [PrIM Benchmarks Source Code] [Slides (pptx) (pdf)] [Talk Video (37 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 229: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 230: Newer Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version] [Slides (pptx) (pdf)] [Talk Video at AACBB 2019]
Oxford Nanopore MinION

## Slide 231: New Applications: Graph Genomes
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 232: New Applications: Ref Genome Updates
https://people.inf.ethz.ch/omutlu/pub/AirLift_genome-remapper_arxiv21.pdf

## Slide 233: Newer Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version] [Slides (pptx) (pdf)] [Talk Video at AACBB 2019]
Oxford Nanopore MinION

## Slide 234: Recall: High-Throughput Sequencing
Massively parallel sequencing technology
  Illumina, Roche 454, Ion Torrent, SOLID…
Small DNA fragments are first amplified and then sequenced in parallel, leading to
  High throughput
  High speed
  Low cost
  Short reads
    Amplification step limits the read length since too short or too long fragments are not amplified well.
Sequencing is done by either reading optical signals as each base is added, or by detecting hydrogen ions instead of light, leading to:
  Low error rates (relatively)
  Reads lack information about their order and which part of genome they are originated from

## Slide 235: Nanopore Sequencing Technology
Nanopore sequencing is an emerging and a promising single-molecule DNA sequencing technology
First nanopore sequencing device, MinION, made commercially available by Oxford Nanopore Technologies (ONT) in May 2014.
  Inexpensive
  Long read length (> 882K bp)
  Portable: Pocket-sized
  Produces data in real-time
Notes: MinION is an inexpensive, pocket-sized, portable, high-throughput sequencing apparatus that produces data in real-time. These properties enable new potential applications of genome sequencing, such as rapid surveillance of Ebola, Zika or other epidemics, near-patient testing, and other applications that require real- time data analysis.
In addition, the MinION technology has two major advantages. First, it is capable of generating ultra-long reads (e.g., 882 kilobase pairs or longer). MinION’s long reads greatly simplify the genome assembly process by decreasing the computational requirements. Second, it is small and portable. MinION is named as the first DNA sequencing device used in outer space to help the detection of life elsewhere in the universe with the help of its size and portability.
With the help of continuous updates to the MinION device and the nanopore chemistry, the first nanopore human reference genome was generated by using only MinION devices.

## Slide 236: Nanopore Sequencing Technology
Nanopore sequencing is an emerging and a promising single-molecule DNA sequencing technology
  No amplification → Less limit on read length → Longer read length
First nanopore sequencing device, MinION, made commercially available by Oxford Nanopore Technologies (ONT) in May 2014.
  Inexpensive
  Long read length (> 882K bp)
  Portable: Pocket-sized
  Produces data in real-time
Notes: MinION is an inexpensive, pocket-sized, portable, high-throughput sequencing apparatus that produces data in real-time. These properties enable new potential applications of genome sequencing, such as rapid surveillance of Ebola, Zika or other epidemics, near-patient testing, and other applications that require real- time data analysis.
In addition, the MinION technology has two major advantages. First, it is capable of generating ultra-long reads (e.g., 882 kilobase pairs or longer). MinION’s long reads greatly simplify the genome assembly process by decreasing the computational requirements. Second, it is small and portable. MinION is named as the first DNA sequencing device used in outer space to help the detection of life elsewhere in the universe with the help of its size and portability.
With the help of continuous updates to the MinION device and the nanopore chemistry, the first nanopore human reference genome was generated by using only MinION devices.

## Slide 237: Oxford Nanopore Sequencers
https://nanoporetech.com/products/comparison
 | MinION Mk1B | MinION Mk1C | GridION Mk1 | PromethION 24 | PromethION 48
Read length | > 2Mb | > 2Mb | > 2Mb | > 2Mb | > 2Mb
Yield per flow cell | 50 Gb | 50 Gb | 50 Gb | 220 Gb | 220 Gb
Number of flow cells per device | 1 | 1 | 5 | 24 | 48
Yield per device | <50 Gb | <50 Gb | <250 Gb | <5.2 Tb | <10.5 Tb
Starting price | $1,000 | $4,990 | $49,995 | $195,455 | $327,455

## Slide 238: Illumina Sequencers
Run time | 9.5–19 hrs | 4–24 hrs | 4–55 hrs | 12–30 hrs | 24-48 hrs | 13-44 hrs
Max. reads per run | 4 million | 25 million | 25 million | 400 million | 1 billion | 20 billion
Max. read length | 2 × 150 bp | 2 × 150 bp | 2 × 300 bp | 2 × 150 bp | 2 × 150 bp | 2 x 250
Max. output | 1.2 Gb | 7.5 Gb | 15 Gb | 120 Gb | 300 Gb | 6000 Gb
Estimated price | $19,900 | $49,500 | $128,000 | $275,000 | $335,000 | $985,000
https://www.illumina.com/systems/sequencing-platforms.html

## Slide 239: How Does Nanopore Sequencing Work?
Nanopore is a nano-scale hole (<20nm).
In nanopore sequencers, an ionic current passes through the nanopores
When the DNA strand passes through the nanopore, the sequencer measures the the change in current
This change is used to identify the bases in the strand with the help of different electrochemical structures of the different bases
graphene nanopore
DNA strand
Figure is adapted from: https://phys.org/news/2013-12-gene-sequencing-future.html

## Slide 240: Advantages of Nanopore Sequencing
Nanopores:
Do not require any labeling of the DNA or nucleotide for detection during sequencing
Rely on the electronic or chemical structure of the different nucleotides for identification
Allow sequencing very long reads, and
Provide portability, low cost, and high throughput.

## Slide 241: Challenges of Nanopore Sequencing
One major drawback: high error rates
Nanopore sequence analysis tools have a critical role to:
  overcome high error rates
  take better advantage of the technology
Faster tools are critically needed to:
  Take better advantage of the real-time data production capability of nanopore sequencing
  Enable fast, real-time data analysis

## Slide 242: Nanopore Genome Assembly Pipeline
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly” Briefings in Bioinformatics, 2018.

## Slide 243: Nanopore Genome Assembly Tools (I)
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly” Briefings in Bioinformatics, 2018.

## Slide 244: Nanopore Genome Assembly Tools (II)
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly” Briefings in Bioinformatics, 2018.

## Slide 245: Nanopore Genome Assembly Tools (III)
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly” to appear in Briefings in Bioinformatics, 2018.

## Slide 246: More on Nanopore Sequencing & Tools
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
BiB arXiv

## Slide 247: Why Do We Care? An Example from 2020
Source: https://nanoporetech.com/about-us/news/200-oxford-nanopore-sequencers-have-left-uk-china-support-rapid-near-sample

## Slide 248: Sequencing of COVID-19
Whole genome sequencing (WGS) and sequence data analysis are important
  To detect the virus from a human sample such as saliva, Bronchoalveolar fluid etc.
  To understand the sources and modes of transmission of the virus
  To discover the genomic characteristics of the virus, and compare with better-known viruses (e.g., 02-03 SARS epidemic)
  To design and evaluate the diagnostic tests and deep-dive studies
Two key areas of COVID-19 genomic research
  To sequence the genome of the virus itself, COVID-19, in order to track the mutations in the virus.
  To explore the genes of infected patients. This analysis can be used to understand why some people get more severe symptoms than others, as well as, help with the development of new treatments in the future.

## Slide 249: COVID-19 Nanopore Sequencing (I)
From ONT (https://nanoporetech.com/covid-19/overview)

## Slide 250: COVID-19 Nanopore Sequencing (II)
From ONT (https://nanoporetech.com/covid-19/overview)

## Slide 251: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 252: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 253: Conclusion

## Slide 254: Recall Our Dream (from 2007)
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
Still a long ways to go
  Energy efficiency
  Performance (latency)
  Security & privacy
  Huge memory bottleneck

## Slide 255: Conclusion
System design for bioinformatics is a critical problem
  It has large scientific, medical, societal, personal implications
This talk is about accelerating a key step in bioinformatics: genome sequence analysis
  In particular, read mapping
We covered various recent ideas to accelerate read mapping
  My personal journey since September 2006
Many future opportunities exist
  Especially with new sequencing technologies
  Especially with new applications and use cases

## Slide 256: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 257: Resources & Acknowledgments

## Slide 258: Accelerating Genome Analysis: Overview
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 259: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 260: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 261: More on Memory-Centric System Design
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 262: A Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=H3sEaINPBOE

## Slide 263: Detailed Lectures on Genome Analysis
Computer Architecture, Fall 2020, Lecture 3a
  Introduction to Genome Sequence Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=CrRb32v7SJc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=5
Computer Architecture, Fall 2020, Lecture 8
  Intelligent Genome Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=ygmQpdDTL7o&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=14
Computer Architecture, Fall 2020, Lecture 9a
  GenASM: Approx. String Matching Accelerator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=XoLpzmN-Pas&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=15
Accelerating Genomics Project Course, Fall 2020, Lecture 1
  Accelerating Genomics (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=rgjl8ZyLsAg&list=PL5Q2soXY2Zi9E2bBVAgCqLgwiDRQDTyId
https://www.youtube.com/onurmutlulectures

## Slide 264: A Longer Version of This Lecture…
Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" Invited Lecture at Technion, Virtual, 26 January 2021. [Slides (pptx) (pdf)] [Talk Video (1 hour 37 minutes, including Q&A)] [Related Invited Paper (at IEEE Micro, 2020)]

## Slide 265: Comp Arch (Fall 2021)
Fall 2021 Edition:
  https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Fall 2020 Edition:
  https://safari.ethz.ch/architecture/fall2020/doku.php?id=schedule
Youtube Livestream (2021):
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Youtube Livestream (2020):
  https://www.youtube.com/watch?v=c3mPdZA-Fmc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 266: DDCA (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2022/doku.php?id=schedule
Spring 2021 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2021/doku.php?id=schedule
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=cpXdE3HwvK0&list=PL5Q2soXY2Zi97Ya5DEUpMpO2bbAoaG7c6
Youtube Livestream (Spring 2021):
  https://www.youtube.com/watch?v=LbC0EZY8yw4&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN
Bachelor’s course
  2nd semester at ETH Zurich
  Rigorous introduction into “How Computers Work”
  Digital Design/Logic
  Computer Architecture
  10 FPGA Lab Assignments
https://www.youtube.com/onurmutlulectures

## Slide 267: Seminar in Comp Arch (Spring & Fall)
Spring 2022 Edition:
  https://safari.ethz.ch/architecture_seminar/spring2022/doku.php?id=schedule
Fall 2021 Edition:
  https://safari.ethz.ch/architecture_seminar/fall2021/doku.php?id=schedule
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=rS9UPk509AQ&list=PL5Q2soXY2Zi_hxizriwKmFHgcoe2Q8-m0
Youtube Livestream (Fall 2021):
  https://www.youtube.com/watch?v=4TcP297mdsI&list=PL5Q2soXY2Zi_7UBNmC9B8Yr5JSwTG9yH4
Critical analysis course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  20+ research papers, presentations, analyses

## Slide 268: PIM Course (Fall 2021)
Fall 2021 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2021/doku.php?id=processing_in_memory
Youtube Livestream:
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings

## Slide 269: PIM Course (Current)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream:
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings

## Slide 270: Genomics (Spring 2022)
Fall 2021 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=bioinformatics
Youtube Livestream:
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi8NrPDgOR1yRU_Cxxjw-u18
Project course
  Taken by Bachelor’s/Master’s students
  Genomics lectures
  Hands-on research exploration
  Many research readings

## Slide 271: Genomics (Fall 2021)
Fall 2021 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2021/doku.php?id=bioinformatics
Youtube Livestream:
  https://www.youtube.com/watch?v=MnogTeMjY8k&list=PL5Q2soXY2Zi8sngH-TrNZnDhDkPq55J9J
Project course
  Taken by Bachelor’s/Master’s students
  Genomics lectures
  Hands-on research exploration
  Many research readings

## Slide 272: Funding Acknowledgments
Alibaba, AMD, ASML, Google, Facebook, Hi-Silicon, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware, Xilinx
NSF
NIH
GSRC
SRC
CyLab
EFCL

## Slide 273: Acknowledgments
Think BIG, Aim HIGH!
https://safari.ethz.ch

## Slide 274
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 275: SAFARI Newsletter April 2020 Edition
https://safari.ethz.ch/safari-newsletter-april-2020/

## Slide 276: SAFARI Newsletter January 2021 Edition
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 277: SAFARI Newsletter December 2021 Edition
https://safari.ethz.ch/safari-newsletter-december-2021/

## Slide 278: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 279: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 280: Accelerating Genome Analysis A Primer on an Ongoing Journey
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
18 June 2022
AACBB Workshop Keynote @ ISCA 2022

## Slide 281: Backup Slides for Further Info

## Slide 282: Detailed Lectures on PIM (I)
Computer Architecture, Fall 2020, Lecture 6
  Computation in Memory (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=oGcZAGwfEUE&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=12
Computer Architecture, Fall 2020, Lecture 7
  Near-Data Processing (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=j2GIigqn1Qw&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=13
Computer Architecture, Fall 2020, Lecture 11a
  Memory Controllers (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=TeG773OgiMQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=20
Computer Architecture, Fall 2020, Lecture 12d
  Real Processing-in-DRAM with UPMEM (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=25
https://www.youtube.com/onurmutlulectures

## Slide 283: Detailed Lectures on PIM (II)
Computer Architecture, Fall 2020, Lecture 15
  Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=AlE1rD9G_YU&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=28
Computer Architecture, Fall 2020, Lecture 16a
  Opportunities & Challenges of Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=pmLszWGmMGQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=29
Computer Architecture, Fall 2020, Guest Lecture
  In-Memory Computing: Memory Devices & Applications (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=wNmqQHiEZNk&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=41
https://www.youtube.com/onurmutlulectures

## Slide 284: Genome Analysis
>CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCCAAGAGTTGCAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTAGCCAGAATGGTTGTGGGATGGGAGCCTCTGTGGACCGACCAGGTAGCTCTCTTTTCCACACTGTAGTCTCAAAGCTTCTTCATGTGGTTTCTCTGAGTGAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTTTTCATGTCAAGGACCTAATGTAGCTATACTGAACGTTATCTAGGGGAAAGATTGAAGGGGAGCTCTAAGGTCAACACACCACCACTTCCCAGAAAGCTTCTTCA……
  machine can read the entire content of a genome
NO
Notes: Why we can not do that?
Challenges: 1- supercoiled structure, small cell’s size, sensitivity to 1 base, DNA length.

## Slide 285: Genome Analysis
>CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCCAAGAGTTGCAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTAGCCAGAATGGTTGTGGGATGGGAGCCTCTGTGGACCGACCAGGTAGCTCTCTTTTCCACACTGTAGTCTCAAAGCTTCTTCATGTGGTTTCTCTGAGTGAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTTTTCATGTCAAGGACCTAATGTAGCTATACTGAACGTTATCTAGGGGAAAGATTGAAGGGGAGCTCTAAGGTCAACACACCACCACTTCCCAGAAAGCTTCTTCA……
  machine can read the entire content of a genome
NO
Why?
Notes: Why we can not do that?
Challenges: 1- supercoiled structure, small cell’s size, sensitivity to 1 base, DNA length.

## Slide 286: Genome Sequencer is a Chopper
Genome Analysis
44 hours
1x1012 bases
* NovaSeq 6000
*
*
GATK
<1000 $
Notes: Reads lack information about their order and location (which part of genome they are originated from)
PICO bases/44 hours

## Slide 287: Oxford Nanopore Sequencers
https://nanoporetech.com/products/comparison
 | MinION Mk1B | MinION Mk1C | GridION Mk1 | PromethION 24 | PromethION 48
Read length | > 2Mb | > 2Mb | > 2Mb | > 2Mb | > 2Mb
Yield per flow cell | 50 Gb | 50 Gb | 50 Gb | 220 Gb | 220 Gb
Number of flow cells per device | 1 | 1 | 5 | 24 | 48
Yield per device | <50 Gb | <50 Gb | <250 Gb | <5.2 Tb | <10.5 Tb
Starting price | $1,000 | $4,990 | $49,995 | $195,455 | $327,455

## Slide 288: Illumina Sequencers
Run time | 9.5–19 hrs | 4–24 hrs | 4–55 hrs | 12–30 hrs | 24-48 hrs | 13-44 hrs
Max. reads per run | 4 million | 25 million | 25 million | 400 million | 1 billion | 20 billion
Max. read length | 2 × 150 bp | 2 × 150 bp | 2 × 300 bp | 2 × 150 bp | 2 × 150 bp | 2 x 250
Max. output | 1.2 Gb | 7.5 Gb | 15 Gb | 120 Gb | 300 Gb | 6000 Gb
Estimated price | $19,900 | $49,500 | $128,000 | $275,000 | $335,000 | $985,000
https://www.illumina.com/systems/sequencing-platforms.html

## Slide 289: How Does Illumina Machine Work?
T
Glass flow
cell surface
The sequencer adds the molecule “T” to all bases near the flow cell surface and observes the chemical reaction via a CMOS sensor. If a reaction happens then the base is “A”
T
C
A
G
T
A
C
A
T
Optical Sensor
A
Notes: Until today, there is no machine takes genomic sample and produces the full sequence of the donor. I
nstead, HTS technology is used to sequence/read random short DNA fragments of copies of the original molecule.
The sequencer adds the molecule “T” to all bases near the flow cell surface and observes the chemical reaction by a CMOS sensor. If a reaction happens then the base is “A” (A reacts with T, C with G and vice versa).
This step is repeated for A, C, and G molecules for each base of the fragments.
Bases are sequenced concurrently, hence the name “high throughput”.

## Slide 290: How Does Illumina Machine Work?
A
C
G
C
C
C
G
T
G
C
G
T
A
C
G
T
A
C
G
T
A
C
G
C
A
C
G
T
A
A
G
A
A
C
G
T
A
C
G
T
A
C
G
T
A
C
G
A
A
C
G
T
A
C
G
T
A
C
G
T
G
C
G
G
A
C
G
T
A
C
G
T
A
C
G G G C
G
C
G
C
G
T
A
C
G
C
A
C
G
T
A
C
G
T
A
C
G
T
A
C
G
T
T
T
T
T
A
C
G
T
T
G
C
Glass flow
cell surface
The sequencer adds the molecule “T” to all bases near the flow cell surface and observes the chemical reaction via a CMOS sensor. If a reaction happens then the base is “A”
A
T
C
A
G
T
A
C
A
T
Optical Sensor
DNA fragment = Read
Notes: Until today, there is no machine takes genomic sample and produces the full sequence of the donor. I
nstead, HTS technology is used to sequence/read random short DNA fragments of copies of the original molecule.
The sequencer adds the molecule “T” to all bases near the flow cell surface and observes the chemical reaction by a CMOS sensor. If a reaction happens then the base is “A” (A reacts with T, C with G and vice versa).
This step is repeated for A, C, and G molecules for each base of the fragments.
Bases are sequenced concurrently, hence the name “high throughput”.

## Slide 291: How Does Illumina Machine Work?
A
C
G
C
C
C
G
T
G
C
G
T
A
C
G
T
A
C
G
T
A
C
G
C
A
C
G
T
A
A
G
A
A
C
G
T
A
C
G
T
A
C
G
T
A
C
G
A
A
C
G
T
A
C
G
T
A
C
G
T
G
C
G
G
A
C
G
T
A
C
G
T
A
C
G G G C
G
C
G
C
G
T
A
C
G
C
A
C
G
T
A
C
G
T
A
C
G
T
A
C
G
T
T
T
T
T
A
C
G
T
T
G
C
Glass flow
cell surface
The sequencer adds the molecule “T” to all bases near the flow cell surface and observes the chemical reaction via a CMOS sensor. If a reaction happens then the base is “A”
A
T
C
A
G
T
A
C
A
T
Optical Sensor
DNA fragment = Read
Check Illumina virtual tour:
https://emea.illumina.com/systems/sequencing-platforms/iseq/tour.html
Notes: Until today, there is no machine takes genomic sample and produces the full sequence of the donor. I
nstead, HTS technology is used to sequence/read random short DNA fragments of copies of the original molecule.
The sequencer adds the molecule “T” to all bases near the flow cell surface and observes the chemical reaction by a CMOS sensor. If a reaction happens then the base is “A” (A reacts with T, C with G and vice versa).
This step is repeated for A, C, and G molecules for each base of the fragments.
Bases are sequenced concurrently, hence the name “high throughput”.

## Slide 292: How Does Nanopore Machine Work?
Nanopore is a nano-scale hole (<20nm).
In nanopore sequencers, an ionic current passes through the nanopores
When the DNA strand passes through the nanopore, the sequencer measures the the change in current
This change is used to identify the bases in the strand with the help of different electrochemical structures of the different bases
graphene nanopore
DNA strand
Figure is adapted from: https://phys.org/news/2013-12-gene-sequencing-future.html

## Slide 293: How Does Nanopore Machine Work?
Nanopore is a nano-scale hole (<20nm).
In nanopore sequencers, an ionic current passes through the nanopores
When the DNA strand passes through the nanopore, the sequencer measures the the change in current
This change is used to identify the bases in the strand with the help of different electrochemical structures of the different bases
graphene nanopore
DNA strand
Figure is adapted from: https://phys.org/news/2013-12-gene-sequencing-future.html
Check Nanopore virtual tour:
https://nanoporetech.com/resource-centre/minion-video

## Slide 294: Solving the Puzzle
https://www.pacb.com/smrt-science/smrt-sequencing/hifi-reads-for-highly-accurate-long-read-sequencing/
Reads
Reference genome
Notes: Rhinoceros

## Slide 295: HTS Sequencing Output
500-2M bp
high error rate (~15%)
100-300 bp
low error rate (~0.1%)
Large pieces of a puzzle
long reads (ONT & PacBio)
Small pieces of a puzzle
short reads (Illumina)
Which sequencing technology is the best?
https://www.pacb.com/smrt-science/smrt-sequencing/hifi-reads-for-highly-accurate-long-read-sequencing/

## Slide 296: HiFi Reads (PacBio)
Wenger+, "Accurate circular consensus long-read sequencing improves variant detection and assembly of a human genome", Nature Biotechnology, 2019
But still very expensive!
https://labs.wsu.edu/genomicscore/illumina-sequencing/
https://pacbio.gs.washington.edu/
Long: 10-20 kb
Accurate: 99.8%
Notes: By sequencing the same DNA segment many times (10 to 30 times), we can have accurate more longer reads.

## Slide 297: How Long is DNA?
Phi X174 virus
5.386 Killo bp
E. coli O157:H7
5.44 Million bp
Homo Sapiens
3.2 Billion bp
Onion, Allium Cepa
16 Billion bp
Paris Japonica
149 Billion bp
Notes: Phi x174 is a virus that Infects E. Coli bacteria
You may be exposed to E. coli from contaminated water or food — especially raw vegetables and undercooked ground beef.
Paris Japonica : A rare Japanese flower
============================
Phi is 600K time smaller than the genome of human
E coli is ~600 time smaller than the human genome
Onion has a genome that is 5x larger than that of human
Paris japonica’s genome is 46x larger than the human genome

## Slide 298: Cracking the 1st Human Genome Sequence
1990-2003: The Human Genome Project (HGP) provides a complete and accurate sequence of all DNA base pairs that make up the human genome and finds 20,000 to 25,000 human genes.
13 years
3.2 x109
bases
>3x109 $
Notes: The 13-year long human project is the starting of the genomic era! It opened the door to remarkable biomedical discoveries by providing the first complete human genome sequence. It cost 3 billion dollars to read the entire sequence.

## Slide 299: Obtaining the Human Reference Genome
GRCh38.p13
Description: Genome Reference Consortium Human Build 38 patch release 13 (GRCh38.p13)
Organism name: Homo sapiens (human)
Date: 2019/02/28
3,099,706,404 bases
Compressed .fna file (964.9 MB)
https://www.ncbi.nlm.nih.gov/assembly/GCF_000001405.39
>NC_000001.11 Homo sapiens chromosome 1, GRCh38.p13 Primary Assembly NNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNN NNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNN NNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNN NNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNNN

## Slide 300: Challenges in Read Mapping
Need to find many mappings of each read
Need to tolerate variances/sequencing errors in each read
Need to map each read very fast (i.e., performance is important, life critical in some cases)
Need to map reads to both forward and reverse strands
https://www.bioinformaticsalgorithms.org/bioinformatics-chapter-1
Notes: There are three main challenges.
First. The mapper needs to find many mappings for each read. Because the read is so short, they can map to multiple locations in the reference genome. How can we efficiently find all mappings of a read?
Second. The mapper needs to tolerate small variance or errors in each read. Since individuals are different, the subject’s DNA might slightly differs from the reference DNA, which can be mismatches, insertions or deletions of base pairs. How can we efficiently map each read with up to a number of e errors present?
Third. The mapper needs to map each read very fast. In another word, performance is important. Because the human DNA is 3.2 billion base-pairs long and each read is only hundreds of base-pairs long, there can be billions of reads subjected to mapping for an individual human. Current state of the art mappers take weeks to map a human’s DNA. So the question is, how can we design a much higher performance read mapper?

## Slide 301: Revisiting the Puzzle
https://www.pacb.com/smrt-science/smrt-sequencing/hifi-reads-for-highly-accurate-long-read-sequencing/

## Slide 302: Reference Genome Bias
Sherman+, “Assembly of a pan-genome from deep sequencing of 910 humans of African descent” Nature genetics, 2019.
“African pan-genome contains ~10% more DNA bases than the current human reference genome”

## Slide 303: Time to Change the Reference Genome
“Switching to a consensus reference would offer important advantages over the continued use of the current reference with few disadvantages”
Ballouz+, "Is it time to change the reference genome?", Genome Biology, 2019
Notes: a consensus reference represents the most common nucleotide at each position.

## Slide 304: MAGNET (AACBB 2018, TIR 2017)
Key observation: the use of AND operation to check if a zero (match) exists in a column introduces filtering inaccuracy.
Key Idea: count the consecutive zeros in each mask and select the longest in a divide-and-conquer approach.
MAGNET is 17x to 105x more accurate than GateKeeper and SHD.
Notes: MAGNET will be presented in the next talk.

## Slide 305: MAGNET Walkthrough
Build Neighborhood Map
Track the Diagonally Consecutive Matches
ACCEPT iff number of ‘1’ ≤ Threshold
Exclude the errors from the search space
Divide the problem into two subproblems and repeat
Find the longest segment of consecutive zeros
"MAGNET: understanding and improving the accuracy of genome pre-alignment filtering", arXiv preprint 2017
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 306
What if we got a new version of the reference genome?

## Slide 307: AirLift
Key observation: Reference genomes are updated frequently. Repeating read mapping is a computationally expensive workload.
Key idea: Update the mapping results of only affected reads depending on how a region in the old reference relates to another region in the new reference.
Key results:
  reduces number of reads that needs to be re-mapped to new reference by up to 99%
  reduces overall runtime to re-map reads by 6.94x, 208x, and 16.4x for large (human), medium (C. elegans), and small (yeast) reference genomes

## Slide 308: Clustering the Reference Genome Regions

## Slide 309: More Details on AirLift
GitHub: https://github.com/CMU-SAFARI/AirLift
Kim+, "AirLift: A Fast and Comprehensive Technique for Translating Alignments between Reference Genomes", arXiv, 2020

## Slide 310: Nanopore Sequencing
Nanopore is a nano-scale hole
In nanopore sequencers, an ionic current passes through the nanopores
When the DNA strand passes through the nanopore, the sequencer measures the the change in current
This change is used to identify the bases in the strand with the help of different electrochemical structures of the different bases

## Slide 311: The Effect of Pre-Alignment (Theoretically)
Chart: Pre-alignment rejected mapping percentage and speed compared to alignment step
| 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 2x | 4x | 8x | 16x | 32x | 64x | 128x | 256x
Total processing time without pre-alignment (sec) | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000
Chart: Pre-alignment rejected mapping percentage and speed compared to alignment step
| 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 100% | 80% | 60% | 40% | 20% | 2x | 4x | 8x | 16x | 32x | 64x | 128x | 256x
Total processing time without pre-alignment (sec) | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000 | 10000
Total processing time with pre-alignment (sec) | 5000 | 7000 | 9000 | 11000 | 13000 | 2500 | 4500 | 6500 | 8500 | 10500 | 1250 | 3250 | 5250 | 7250 | 9250 | 625 | 2625 | 4625 | 6625 | 8625 | 312.5 | 2312.5 | 4312.5 | 6312.5 | 8312.5 | 156.25 | 2156.25 | 4156.25 | 6156.25 | 8156.25 | 78.125 | 2078.125 | 4078.125 | 6078.125 | 8078.125 | 39.0625 | 2039.0625 | 4039.0625 | 6039.0625 | 8039.0625
Ideal processing time for 90% pre-alignment rejection percentage | 6000 | 6000 | 6000 | 6000 | 6000 | 3500 | 3500 | 3500 | 3500 | 3500 | 2250 | 2250 | 2250 | 2250 | 2250 | 1625 | 1625 | 1625 | 1625 | 1625 | 1312.5 | 1312.5 | 1312.5 | 1312.5 | 1312.5 | 1156.25 | 1156.25 | 1156.25 | 1156.25 | 1156.25 | 1078.125 | 1078.125 | 1078.125 | 1078.125 | 1078.125 | 1039.0625 | 1039.0625 | 1039.0625 | 1039.0625 | 1039.0625
assuming alignment processes 100 Mappings/sec
Filter+
Alignment
Target
Pre-alignment saves more than
40% to 80%
of the total processing time
Notes: What effect pre-alignment has on overall execution time? Well, that depends on how much and how fast it can remove incorrect mappings
We make
two key observations. (1) The reduction in the end-to-end processing time of the
alignment step largely depends on the accuracy and the speed of the pre-alignment
lter. (2) Pre-alignment ltering can provide unsatisfactory performance (as
highlighted in red) if it can not reject more than about 30% of the potential
mappings while it's only 2x-4x faster than read alignment step.

## Slide 312: Aside: In-Memory Graph Processing
Large graphs are everywhere (circa 2015)
Scalable large-scale graph processing is challenging
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos
Chart: Speedup
| 128 Cores | 32 Cores
열3 | 1.4206 | 1

## Slide 313: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 314: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 315: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communications via Remote Function Calls

## Slide 316: Communications In Tesseract (I)

## Slide 317: Communications In Tesseract (II)

## Slide 318: Communications In Tesseract (III)

## Slide 319: Remote Function Call (Non-Blocking)

## Slide 320: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 321: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
Tesseract
32 Tesseract Cores
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 322: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
On five graph processing algorithms

## Slide 323: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
Chart: Memory Bandwidth Consumption
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 0.079545 | 0.1904 | 0.24289 | 1.2943 | 2.244 | 2.9197

## Slide 324: Effect of Bandwidth & Programming Model
Chart: Speedup
| HMC-MC | HMC-MC + PIM BW | Tesseract + Conventional BW | Tesseract
계열 1 | 1 | 2.3043 | 3.0224 | 6.4999
HMC-MC Bandwidth (640GB/s)
Tesseract Bandwidth (8TB/s)
Bandwidth
Programming Model
(No Prefetching)

## Slide 325: Tesseract Graph Processing System Energy
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
> 8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 326: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 327: End of Backup Slides