## Slide 1: Scalable Many-Core Memory Systems Optional Topic 4: Cache Management
Prof. Onur Mutlu
http://www.ece.cmu.edu/~omutlu
onur@cmu.edu
HiPEAC ACACES Summer School 2013
July 15-19, 2013

## Slide 2: What Will You Learn in This Course?
Scalable Many-Core Memory Systems
  July 15-19, 2013
Topic 1: Main memory basics, DRAM scaling
Topic 2: Emerging memory technologies and hybrid memories
Topic 3: Main memory interference and QoS
Topic 4 (unlikely): Cache management
Topic 5 (unlikely): Interconnects
Major Overview Reading:
  Mutlu, “Memory Scaling: A Systems Architecture Perspective,” IMW 2013.

## Slide 3: Readings and Videos

## Slide 4: Readings for Topic 4
Required – Caches in Multi-Core
  Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2005.
  Seshadri et al., “The Evicted-Address Filter: A Unified Mechanism to Address both Cache Pollution and Thrashing,” PACT 2012.
  Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.
  Pekhimenko et al., “Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency,” SAFARI Technical Report 2013.
Recommended
  Qureshi et al., “Utility-Based Cache Partitioning: A Low-Overhead, High-Performance, Runtime Mechanism to Partition Shared Caches,” MICRO 2006.

## Slide 5: Videos for Lecture Topic 4
Cache basics:
  http://www.youtube.com/watch?v=TpMdBrM1hVc&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=23
Advanced caches:
  http://www.youtube.com/watch?v=TboaFbjTd-E&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=24

## Slide 6: Online Lectures and More Information
Online Computer Architecture Lectures
  http://www.youtube.com/playlist?list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ
Online Computer Architecture Courses
  Intro: http://www.ece.cmu.edu/~ece447/s13/doku.php
  Advanced: http://www.ece.cmu.edu/~ece740/f11/doku.php
  Advanced: http://www.ece.cmu.edu/~ece742/doku.php
Recent Research Papers
  http://users.ece.cmu.edu/~omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en

## Slide 7: Shared Resource Design for Multi-Core Systems

## Slide 8: The Multi-Core System: A Shared Resource View
Shared
Storage

## Slide 9: Resource Sharing Concept
Idea: Instead of dedicating a hardware resource to a hardware context, allow multiple contexts to use it
  Example resources: functional units, pipeline, caches, buses, memory
Why?
+ Resource sharing improves utilization/efficiency  throughput
  When a resource is left idle by one thread, another thread can use it; no need to replicate shared data
+ Reduces communication latency
  For example, shared data kept in the same cache in SMT processors
+ Compatible with the shared memory model

## Slide 10: Resource Sharing Disadvantages
Resource sharing results in contention for resources
  When the resource is not idle, another thread cannot use it
  If space is occupied by one thread, another thread needs to re-occupy it
- Sometimes reduces each or some thread’s performance
- Thread performance can be worse than when it is run alone
- Eliminates performance isolation  inconsistent performance across runs
- Thread performance depends on co-executing threads
- Uncontrolled (free-for-all) sharing degrades QoS
- Causes unfairness, starvation
Need to efficiently and fairly utilize shared resources

## Slide 11: Need for QoS and Shared Resource Mgmt.
Why is unpredictable performance (or lack of QoS) bad?
Makes programmer’s life difficult
  An optimized program can get low performance (and performance varies widely depending on co-runners)
Causes discomfort to user
  An important program can starve
  Examples from shared software resources
Makes system management difficult
  How do we enforce a Service Level Agreement when hardware resources are sharing is uncontrollable?

## Slide 12: Resource Sharing vs. Partitioning
Sharing improves throughput
  Better utilization of space
Partitioning provides performance isolation (predictable performance)
  Dedicated space
Can we get the benefits of both?
Idea: Design shared resources such that they are efficiently utilized, controllable and partitionable
  No wasted resource + QoS mechanisms for threads

## Slide 13: Shared Hardware Resources
Memory subsystem (in both MT and CMP)
  Non-private caches
  Interconnects
  Memory controllers, buses, banks
I/O subsystem (in both MT and CMP)
  I/O, DMA controllers
  Ethernet controllers
Processor (in MT)
  Pipeline resources
  L1 caches

## Slide 14: Multi-core Issues in Caching
How does the cache hierarchy change in a multi-core system?
Private cache: Cache belongs to one core (a shared block can be in multiple caches)
Shared cache: Cache is shared by multiple cores
CORE 0
CORE 1
CORE 2
CORE 3
L2
CACHE
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
L2
CACHE
CORE 0
CORE 1
CORE 2
CORE 3
DRAM MEMORY CONTROLLER
L2
CACHE

## Slide 15: Shared Caches Between Cores
Advantages:
  High effective capacity
  Dynamic partitioning of available cache space
    No fragmentation due to static partitioning
  Easier to maintain coherence (a cache block is in a single location)
  Shared data and locks do not ping pong between caches
Disadvantages
  Slower access
  Cores incur conflict misses due to other cores’ accesses
    Misses due to inter-core interference
    Some cores can destroy the hit rate of other cores
  Guaranteeing a minimum level of service (or fairness) to each core is harder (how much space, how much bandwidth?)

## Slide 16: Shared Caches: How to Share?
Free-for-all sharing
  Placement/replacement policies are the same as a single core system (usually LRU or pseudo-LRU)
  Not thread/application aware
  An incoming block evicts a block regardless of which threads the blocks belong to
Problems
  Inefficient utilization of cache: LRU is not the best policy
  A cache-unfriendly application can destroy the performance of a cache friendly application
  Not all applications benefit equally from the same amount of cache: free-for-all might prioritize those that do not benefit
  Reduced performance, reduced fairness

## Slide 17: Controlled Cache Sharing
Utility based cache partitioning
  Qureshi and Patt, “Utility-Based Cache Partitioning: A Low-Overhead, High-Performance, Runtime Mechanism to Partition Shared Caches,” MICRO 2006.
  Suh et al., “A New Memory Monitoring Scheme for Memory-Aware Scheduling and Partitioning,” HPCA 2002.
Fair cache partitioning
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.
Shared/private mixed cache mechanisms
  Qureshi, “Adaptive Spill-Receive for Robust High-Performance Caching in CMPs,” HPCA 2009.
  Hardavellas et al., “Reactive NUCA: Near-Optimal Block Placement and Replication in Distributed Caches,” ISCA 2009.

## Slide 18: Efficient Cache Utilization
Qureshi et al., “A Case for MLP-Aware Cache Replacement,” ISCA 2005.
Seshadri et al., “The Evicted-Address Filter: A Unified Mechanism to Address both Cache Pollution and Thrashing,” PACT 2012.
Pekhimenko et al., “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.
Pekhimenko et al., “Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency,” SAFARI Technical Report 2013.

## Slide 19: MLP-Aware Cache Replacement
Moinuddin K. Qureshi, Daniel N. Lynch, Onur Mutlu, and Yale N. Patt, "A Case for MLP-Aware Cache Replacement" Proceedings of the 33rd International Symposium on Computer Architecture (ISCA), pages 167-177, Boston, MA, June 2006. Slides (ppt)

## Slide 20: Memory Level Parallelism (MLP)
Memory Level Parallelism (MLP) means generating and servicing multiple memory accesses in parallel [Glew’98]
Several techniques to improve MLP (e.g., out-of-order execution, runahead execution)
MLP varies. Some misses are isolated and some parallel
How does this affect cache replacement?
time
A
B
C
isolated miss
parallel miss
Notes: Processors are fast, Memory is slow. One way to bridge this gap is to service the memory accesses in parallel. If misses are serviced in parallel, the processor incurs only one long latency stall for all the parallel misses. The notion of generating and servicing off-chip accesses in parallel is termed as Memory Level Parallelism or MLP. Out of order processors improve MLP by continuing processing of independent instructions till the instruction window is full. If there is a miss during the processing of independent instructions, the miss is serviced concurrently with the stalling miss. There are several techniques, such as Runahead, CFP, to improve the MLP of out-of-order processors. MLP is not uniform for all cache misses. Some misses, such as pointer chasing loads, are typically serviced with low MLP while other misses, such as array accesses are serviced with high MLP. Current cache management techniques are not aware of this variation in MLP.

## Slide 21: Traditional Cache Replacement Policies
Traditional cache replacement policies try to reduce miss count
Implicit assumption: Reducing miss count reduces memory-related stall time
Misses with varying cost/MLP breaks this assumption!
Eliminating an isolated miss helps performance more than eliminating a parallel miss
Eliminating a higher-latency miss could help performance more than eliminating a lower-latency miss

## Slide 22: An Example
Misses to blocks P1, P2, P3, P4 can be parallel
Misses to blocks S1, S2, and S3 are isolated
Two replacement algorithms:
  Minimizes miss count (Belady’s OPT)
  Reduces isolated misses (MLP-Aware)
For a fully associative cache containing 4 blocks
S1
P4 P3 P2 P1
P1 P2 P3 P4
S2
S3
Notes: There are 11 memory access instructions in the loop. The accesses to cache blocks P1, P2, P3, P4 occur in the instruction window at same time. If these accesses result in more than 1 miss, then those misses are serviced in parallel. Conversely, misses to the S blocks are spaced far apart in time to misses to the S blocks are always serviced in isolation. This loop executes many times. I will analyze the cache behavior of this loop for two replacement algorithms. The first minimizes the number of misses. The well known Belady's opt algorithm provides a theoretical lower bound on the number of misses. The other is MLP-aware replacement, which tries to reduce the number of isolated misses.

## Slide 23: Fewest Misses = Best Performance
P3
P2
P1
P4
H H H H
M
H H H M
Hit/Miss
Misses=4 Stalls=4
S1
P4 P3 P2 P1
P1 P2 P3 P4
S2
S3
Time
stall
Belady’s OPT replacement
M
M
MLP-Aware replacement
Hit/Miss
P3
P2
S1
P4
P3
P2
P1
P4
P3
P2
S2
P4
P3
P2
S3
P4
S1
S2
S3
P1
P3
P2
S3
P4
S1
S2
S3
P4
H H H
S1
S2
S3
P4
H M M M
H M M M
Time
stall
Misses=6Stalls=2
Saved cycles
Cache
Notes: Although Belady’s OPT minimizes misses, it is impossible to implement it in a real processor as it requires knowledge of the future. We employ the commonly used LRU policy in our experiments

## Slide 24: Motivation
  MLP varies. Some misses more costly than others
  MLP-aware replacement can improve performance by reducing costly misses
Notes: Thus, misses have different MLP. The performance impact of a miss is dependent on its MLP. If this non-uniformity is made visible to the cache replacement engine, then it can reduce improve performance by reducing the number of costly misses.

## Slide 25: Outline
Introduction
MLP-Aware Cache Replacement
  Model for Computing Cost
  Repeatability of Cost
  A Cost-Sensitive Replacement Policy
Practical Hybrid Replacement
  Tournament Selection
  Dynamic Set Sampling
  Sampling Based Adaptive Replacement
Summary
Notes: We have qualitatively talked about some misses being more costly on others. For making decisions based on cost we need a quantitative definition for MLP-Based cost. As a first step to enable MLP-aware cache replacement, we provide a runtime mechanism to compute MLP-Based Cost.

## Slide 26: Computing MLP-Based Cost
Cost of miss is number of cycles the miss stalls the processor
Easy to compute for isolated miss
Divide each stall cycle equally among all parallel misses
A
B
C
t0
t1
t4
t5
time
1
½
1
½
½
t2
t3
½
1
Notes: The cost of a miss can be approximated by the number of cycles the miss stalls the processor. This is easy to measure for isolated miss: every cycle the processor is stalled, the cost of the miss is incremented by 1. For parallel misses, the stalled cycle is divided equally among all parallel misses. The figure shows three misses A, B, and C. Between time t0 and t1, A incurs a cost of 1 cycle, every cycle … This algorithm can easily be implemented in hardware.

## Slide 27: A First-Order Model
Miss Status Holding Register (MSHR) tracks all in flight misses
Add a field mlp-cost to each MSHR entry
Every cycle for each demand entry in MSHR
mlp-cost += (1/N)
N = Number of demand misses in MSHR
Notes: The Miss Status Holding Register ala the MSHR tracks information about all the misses in-flight. Each MSHR entry is added a field, mlp-cost. When the miss enters MSHR, the mlp-cost associated with the miss is initialized to zero. Let N be the number of demand misses in the MSHR. Every cycle, the mlp-cost of each demand miss in MSHR is incremented by 1 over N.

## Slide 28: Machine Configuration
  Processor
    aggressive, out-of-order, 128-entry instruction window
  L2 Cache
    1MB, 16-way, LRU replacement, 32 entry MSHR
  Memory
    400 cycle bank access, 32 banks
  Bus
    Roundtrip delay of 11 bus cycles (44 processor cycles)
Notes: These are the parameters of the baseline configuration used in our experiments. It contains an aggressive out-of-order processor with 128-entry instruction window. The baseline L2 cache is 1 mega byte 16-way and uses the LRU replacement. Memory is 400 cycles away and the bus delay is 44 cycles for roundtrip. Thus an isolated miss takes 444 cycles to get service.

## Slide 29: Distribution of MLP-Based Cost
Cost varies. Does it repeat for a given cache block?
MLP-Based Cost
% of All L2 Misses
Notes: This graph shows the distribution of MLP-based cost for the ammp benchmark. The x axis shows the cost of the miss binned at 60 cycle granularity. The y-axis shows the percentage of all L2 misses. The rightmost bar shows the fraction of misses that have a cost of more than 420 cycles. All isolated misses, and some of the parallel misses serialized because of bank conflicts are accounted for in the right bar. Thus 10% of the misses in ammp are isolated misses. About one third of the misses have a cost between 60 and 120 cycles, denoting an MLP of four. On average, the MLP-based cost of the miss is 185 cycles. (TICK) And such distribution of MLP is true for a wide range of benchmarks. Shown are the distribution of mcf and mgrid. However, to exploit this variation in cost of misses for cost-sensitive replacement, it is important that the cost of the block does not vary significantly between successive misses to the block.

## Slide 30: Repeatability of Cost
  An isolated miss can be parallel miss next time
  Can current cost be used to estimate future cost ?
  Let d = difference in cost for successive miss to a block
    Small d  cost repeats
    Large d  cost varies significantly

## Slide 31: Repeatability of Cost
  In general d is small  repeatable cost
  When d is large (e.g. parser, mgrid)  performance loss
d < 60
59 < d < 120
d > 120

## Slide 32: The Framework
MSHR
L2 CACHE
MEMORY
Quantization of Cost
Computed mlp-based cost is quantized to a 3-bit value
CCL
C
A
R
E
Cost-Aware Repl Engine
Cost Calculation Logic
PROCESSOR
ICACHE
DCACHE
Notes: MLP-aware cache replacement has two components. The cost calculation logic computes the mlp-based cost of each miss using a hardware implementation of the algorithm described earlier. This cost is stored in the tag-store entry of the cache block and is used for cost-aware replacement. To reduce storage overhead the mlp-based cost is quantized into a 3-bit value using the following table and this 3-bit quantized cost is used for replacement decisions.

## Slide 33: Design of MLP-Aware Replacement policy
  A Linear (LIN) function that considers recency and cost
  Victim-LIN = min { Recency (i) + S*cost (i) }
  S = significance of cost. Recency(i) = position in LRU stack cost(i) = quantized cost
  LRU considers only recency and no cost
  Victim-LRU = min { Recency (i) }
  Decisions based only on cost and no recency hurt performance. Cache stores useless high cost blocks

## Slide 34: Results for the LIN policy
  Performance loss for parser and mgrid due to large d
  .

## Slide 35: Effect of LIN policy on Cost
Miss += 4%
IPC += 4%
Miss += 30%
IPC -= 33%
Miss -= 11%
IPC += 22%

## Slide 36: Outline
Introduction
MLP-Aware Cache Replacement
  Model for Computing Cost
  Repeatability of Cost
  A Cost-Sensitive Replacement Policy
Practical Hybrid Replacement
  Tournament Selection
  Dynamic Set Sampling
  Sampling Based Adaptive Replacement
Summary

## Slide 37: Tournament Selection (TSEL) of Replacement Policies for a Single Set
ATD-LIN | ATD-LRU | Saturating Counter (SCTR)
HIT | HIT | Unchanged
MISS | MISS | Unchanged
HIT | MISS | += Cost of Miss in ATD-LRU
MISS | HIT | -= Cost of Miss in ATD-LIN
SET A
SET A
+
SCTR
If MSB of SCTR is 1, MTD uses LIN else MTD use LRU
ATD-LIN
ATD-LRU
SET A
MTD
Notes: We use the tournament selection algorithm commonly employed in branch predictors. The performance of both LIN and LRU are tracked using separate tag directories, called Auxiliary Tag Directory (ATD). ATD-LIN uses the LIN policy and ATD-LRU uses the LRU policy. Each access for the main tag directory are also send to both the ATD’s. A saturating counter is used to track, which of the two policies is performing better. If there is a hit in ATD-LIN and a miss in ATD-LRU the saturating counter is incremented by a value equal to the cost of the miss in LRU. If miss in ATD-LRU and hit in ATD-LIN then the saturating counter is decremented by a value equal to the cost of the miss in LIN. Thus the high bit of the counter is an indicator of which of the two policies, LIN or LRU, is doing better. If the high bit is 1, MTD uses LRU else it uses LIN.
Implementing tournament selection on a per-set basis is expensive as it requires a counter and two extra tag directories for each set.

## Slide 38: Extending TSEL to All Sets
  Implementing TSEL on a per-set basis is expensive
  Counter overhead can be reduced by using a global counter
+
SCTR
Policy for All
Sets In MTD
Set A
ATD-LIN
Set B
Set C
Set D
Set E
Set F
Set G
Set H
Set A
ATD-LRU
Set B
Set C
Set D
Set E
Set F
Set G
Set H
Notes: The overhead of the counter can be reduced by using a single counter to choose a replacement policy for all the sets in the cache. The figure shows how such a mechanism for a cache that has 8 sets. Although the mechanism requires only one counter it still requires overhead of two extra tag directories.

## Slide 39: Dynamic Set Sampling
+
SCTR
Policy for All
Sets In MTD
ATD-LIN
Set B
Set E
Set G
Set B
Set E
Set G
ATD-LRU
Set A
Set A
Set C
Set D
Set F
Set H
Set C
Set D
Set F
Set H
Not all sets are required to decide the best policy Have the ATD entries only for few sets.
Sets that have ATD entries (B, E, G) are called leader sets
Notes: To reduce the overhead of the tag directories, we introduce the dynamic set sampling technique. The key idea is that not all sets are required to decide the best policy. The mechanism can still choose the best policy with a high probability even if only few sets are sampled. The ATD entries are present only for 3 sets, B, E, and G. These sets decide the replacement policy for all sets in the MTD, hence we call these sets as leader sets.

## Slide 40: Dynamic Set Sampling
Bounds using analytical model and simulation (in paper)
DSS with 32 leader sets performs similar to having all sets
Last-level cache typically contains 1000s of sets, thus ATD entries are required for only 2%-3% of the sets
How many sets are required to choose best performing policy?
ATD overhead can further be reduced by using MTD to always simulate one of the policies (say LIN)

## Slide 41: Sampling Based Adaptive Replacement (SBAR)
Decide policy only for follower sets
+
  The storage overhead of SBAR is less than 2KB
  (0.2% of the baseline 1MB cache)
SCTR
MTD
Set B
Set E
Set G
Set G
ATD-LRU
Set A
Set C
Set D
Set F
Set H
Set B
Set E
Leader sets
Follower sets

## Slide 42: Results for SBAR

## Slide 43: SBAR adaptation to phases
  SBAR selects the best policy for each phase of ammp
LIN is better
LRU is better

## Slide 44: Outline
Introduction
MLP-Aware Cache Replacement
  Model for Computing Cost
  Repeatability of Cost
  A Cost-Sensitive Replacement Policy
Practical Hybrid Replacement
  Tournament Selection
  Dynamic Set Sampling
  Sampling Based Adaptive Replacement
Summary

## Slide 45: Summary
  MLP varies. Some misses are more costly than others
  MLP-aware cache replacement can reduce costly misses
  Proposed a runtime mechanism to compute MLP-Based cost and the LIN policy for MLP-aware cache replacement
  SBAR allows dynamic selection between LIN and LRU with low hardware overhead
  Dynamic set sampling used in SBAR also enables other cache related optimizations

## Slide 46: The Evicted-Address Filter
Vivek Seshadri, Onur Mutlu, Michael A. Kozuch, and Todd C. Mowry, "The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing" Proceedings of the 21st ACM International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx)

## Slide 47: Executive Summary
Two problems degrade cache performance
  Pollution and thrashing
  Prior works don’t address both problems concurrently
Goal: A mechanism to address both problems
EAF-Cache
  Keep track of recently evicted block addresses in EAF
  Insert low reuse with low priority to mitigate pollution
  Clear EAF periodically to mitigate thrashing
  Low complexity implementation using Bloom filter
EAF-Cache outperforms five prior approaches that address pollution or thrashing
Notes: …

## Slide 48: Cache Utilization is Important
Core
Last-Level Cache
Memory
Core
Core
Core
Core
Increasing contention
Effective cache utilization is important
Large latency
Notes: All high-performance processors employ on-chip caches.
In most modern systems, multiple cores share the last-level cache.
With the large latency of main memory access and increasing contention between multiple cores, effective cache utilization is critical for system performance.
For effective cache utilization, the cache should be filled with blocks that are likely to be reused.

## Slide 49: Reuse Behavior of Cache Blocks
A
B
C
A
B
C
S
T
U
V
W
X
Y
A
B
C
Different blocks have different reuse behavior
Access Sequence:
High-reuse block
Low-reuse block
Z
Ideal Cache
A
B
C
.
.
.
.
.
Notes: However, different blocks have different reuse behaviors.
For example, consider the following access sequence.
Blocks A, B and C are accessed repeatedly.
We refer to such blocks as High reuse blocks.
On the other hand, the remaining blocks are not reused. We refer to such blocks as low-reuse blocks.
Ideally, the cache should be filled with high-reuse blocks such as A, B and C.
But traditional cache management policies such as LRU suffer from two problems.

## Slide 50: Cache Pollution
H
G
F
E
D
C
B
A
S
H
G
F
E
D
C
B
T
S
H
G
F
E
D
C
U
T
S
H
G
F
E
D
MRU
LRU
LRU Policy
Prior work: Predict reuse behavior of missed blocks. Insert low-reuse blocks at LRU position.
H
G
F
E
D
C
B
A
S
T
U
MRU
LRU
A
B
A
C
B
A
A
S
A
T
S
A
Cache
Problem: Low-reuse blocks evict high-reuse blocks
Notes: The first problem, referred to as cache pollution, is one where blocks with low-reuse evict blocks with high-reuse from the cache.
Consider the following example of a cache following the LRU policy. Although the cache is filled with high–reuse blocks, the LRU policy inserts even blocks with low-reuse at the MRU position, evicting more useful blocks from the cache. So the future accesses to blocks A, B and C will miss in the cache.
To address this problem, prior work proposed the idea of predicting the reuse behavior of missed cache blocks and inserting low-reuse blocks at the LRU position. This mitigates the impact of pollution as shown in the example.

## Slide 51: Cache Thrashing
H
G
F
E
D
C
B
A
I
H
G
F
E
D
C
B
J
I
H
G
F
E
D
C
K
J
I
H
G
F
E
D
MRU
LRU
LRU Policy
A
B
C
D
E
F
G
H
I
J
K
A
B
A
C
B
A
Prior work: Insert at MRU position with a very low probability (Bimodal insertion policy)
Cache
H
G
F
E
D
C
B
A
I
J
K
MRU
LRU
A
I
A
J
I
A
A fraction of working set stays in cache
Cache
Problem: High-reuse blocks evict each other
Notes: The second problem, referred to as thrashing, occurs when the number of high-reuse blocks is more than what the cache can handle, as shown in the example.
In this case, the LRU policy leads to these high-reuse blocks evicting each other from the cache, leading to zero cache hits.
Prior work proposed to achieve this using the bimodal insertion policy, which inserts blocks at the MRU position with a very low probability.
As a result, majority of the blocks are inserted at the LRU position.
For a thrashing working set, this results in a fraction of the working set to be retained in the cache, leading to cache hits for at least that fraction.

## Slide 52: Shortcomings of Prior Works
Prior works do not address both pollution and thrashing concurrently
Prior Work on Cache Pollution
No control on the number of blocks inserted with high priority into the cache
Prior Work on Cache Thrashing
No mechanism to distinguish high-reuse blocks from low-reuse blocks
Our goal: Design a mechanism to address both pollution and thrashing concurrently
Notes: The motivation behind this work is that prior works do not address both pollution and thrashing concurrently.
Prior works on pollution do not have control over the number of high-reuse blocks. As a result, if there are more high-reuse blocks than what the cache can handle, these approaches can suffer from thrashing.
On the other hand, prior works on cache thrashing have no mechanism to distinguish high-reuse blocks from low-reuse blocks. As a result, when a working set is not thrashing, these approaches can suffer from pollution.
Our goal in this work is to design a mechanism to address both cache pollution and thrashing. In this talk, I will present our mechanism, the Evicted-address filter, that achieves our goal.

## Slide 53: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 54: Reuse Prediction
Miss
Missed-block
High reuse
Low reuse
?
Keep track of the reuse behavior of every cache block in the system
Impractical
High storage overhead
Look-up latency
Notes: The reuse prediction problem asks the following question. On a cache miss, does the missed cache block have high reuse or low reuse?
One possible way to answer this question is to keep track of the reuse behavior of every block in the system.
But such an approach is impractical due to its high storage overhead and look-up latency.
So, how do prior works address this problem?

## Slide 55: Prior Work on Reuse Prediction
Use program counter or memory region information.
B
A
T
S
PC 1
PC 2
B
A
T
S
PC 1
PC 2
PC 1
PC 2
C
C
U
U
1. Group Blocks
2. Learn group behavior
3. Predict reuse
Same group → same reuse behavior
No control over number of high-reuse blocks
Notes: Previous approaches proposed to predict the reuse behavior of missed blocks indirectly using program-counter or memory-region information. At a high level, the program-counter based mechanism operates in three steps.
First, the mechanism groups blocks based on the program counter that caused their cache miss.
Second, the mechanism learns the reuse behavior of each group based on the blocks that were previously accessed by the program counter.
Third, the learned behavior of each group is used to predict the reuse behavior of future blocks accessed by the corresponding program counter.
Such an approach has two shortcomings.
First, blocks belonging to the same program counter may not have the same reuse behavior.
Second, the mechanism has no control over the number of blocks predicted to have high reuse. As a result, this approach can potentially suffer from thrashing.

## Slide 56: Our Approach: Per-block Prediction
Use recency of eviction to predict reuse
A
Time
Time of eviction
A
Accessed soon after eviction
S
Time
S
Accessed long time after eviction
Notes: In this work, we propose a mechanism to predict the reuse behavior of a block based on its own past behavior.
The key idea behind our mechanism is to use the recency of eviction of a block to predict its reuse on its next access.
More specifically, if a block is accessed soon after getting evicted, our mechanism concludes that the block was prematurely evicted and predicts it to have high reuse.
On the other hand, if a block is accessed a long time after eviction, our mechanism concludes that the block is unlikely to be accessed in the near future and predicts it to have low reuse.
The above idea suggests that it is sufficient to keep track of a small number of recently evicted blocks to distinguish between high-reuse blocks and low-reuse blocks.

## Slide 57: Evicted-Address Filter (EAF)
Cache
EAF
(Addresses of recently evicted blocks)
Evicted-block address
Miss
Missed-block address
In EAF?
Yes
No
MRU
LRU
High Reuse
Low Reuse
Notes: Based on this observation, our mechanism augments the cache with a structure called the Evicted-address filter that keeps track of addresses of recently evicted blocks.
When a block is evicted from the cache, our mechanism inserts its address into the EAF.
On a cache miss, if the missed block address is present in the EAF, then the block was evicted recently. Therefore, our mechanism predicts that the block has high reuse and inserts it at the MRU position. It also removes the block address from the EAF to create space for more evicted addresses.
On the other hand, if the missed block address is not present in the EAF, there is one of two possibilities: either the block was accessed before and evicted a long time ago or the block is accessed for the first time. In both cases, our mechanism predicts that the block has low reuse and inserts it at the LRU position.
Although the EAF is a simple mechanism to predict the reuse behavior of missed blocks, one natural question is how to implement it in hardware?

## Slide 58: Naïve Implementation: Full Address Tags
EAF
1. Large storage overhead
2. Associative lookups – High energy
Recently evicted address
Need not be 100% accurate
?
Notes: A naïve implementation of the EAF would be to implement it as a tag store where each tag entry corresponds to the address or a recently evicted block.
However, such an implementation suffers from two problems: 1) it has a large storage overhead and 2) it requires associative lookups which consume high energy.
But notice that the EAF need not be 100% accurate as it is just a prediction structure. This raises the possibility of implementing EAF using a more compact structure which doesn’t have the two shortcomings. So, we consider implementing the EAF using a Bloom filter.

## Slide 59: Low-Cost Implementation: Bloom Filter
EAF
Implement EAF using a Bloom Filter
Low storage overhead + energy
Need not be 100% accurate
?
Notes: A naïve implementation of the EAF would be to implement it as a tag store where each tag entry corresponds to the address or a recently evicted block.
However, such an implementation suffers from two problems: 1) it has a large storage overhead and 2) it requires associative lookups which consume high energy.
But notice that the EAF need not be 100% accurate as it is just a prediction structure. This raises the possibility of implementing EAF using a more compact structure which doesn’t have the two shortcomings. So, we consider implementing the EAF using a Bloom filter.

## Slide 60: Bloom Filter
Y
Compact representation of a set
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1. Bit vector
2. Set of hash functions
H1
H2
H1
H2
X
1
1
1
Insert
Test
Z
W
Remove
X
Y
May remove multiple addresses
Clear


False positive
Inserted Elements:
X
Y
Notes: Let me give you a quick overview of a Bloom filter. A Bloom filter is a compact representation of a set, in this case, a set of addresses.
It consists of a bit vector and a set of hash functions.
All the bits in the bit-vector are initialized to zero.
To insert an address X into the set, the Bloom filter computes the values of the two hash functions and sets the corresponding elements in the filter.
To insert another address Y, the Bloom filter repeats the process.
To test if an address is present in the filter, the Bloom filter computes the values of the hash functions and checks if all the corresponding bits are set. If yes, the Bloom filter concludes that the address is present in the set. This is the case for the address X.
However, even if one of the bits is not set, the Bloom filter concludes that the address is not present in the set.
When we test for the address W, the Bloom filter will conclude that W is present in the set. But W was never inserted. The left bit was set due to the insertion of X and the right bit was set due to the insertion of Y. This situation is referred to as a false positive. The false positive rate of a Bloom filter can be made low by controlling the parameters of the Bloom filter.
Since multiple addresses can map to the same bits, a Bloom filter does not support removing individual addresses from the set.
However, all the addresses can be cleared from the set by simply resetting all the bits in the Bloom filter.
Now, let us look at how we can implement EAF using a Bloom filter.

## Slide 61: EAF using a Bloom Filter
EAF
Insert
Test
Evicted-block address
Remove
FIFO address
Missed-block address
Bloom Filter
Remove
If present
when full
Clear




1
2
when full
Bloom-filter EAF: 4x reduction in storage overhead, 1.47% compared to cache size
Notes: Let us quickly revisit the operations performed on the EAF.
First, on a cache eviction, the evicted block address is inserted into the EAF.
Second, on a cahce miss, our mechanism tests if the missed block address is present in the EAF. If yes, the address is also removed from the EAF.
Finally, when the EAF is full, an address is removed in a FIFO manner to create space for more recently evicted addresses.
A Bloom filter based implementation of EAF will support the insert and the test operations.
However, as we saw in the previous slide, the Bloom filter does not support the remove operations. So we need to somehow eliminate these remove operations. For this purpose, we propose two changes to the EAF design.
First, on a cache miss, if the missed block address is present in the EAF, we choose to retain the block address in the EAF instead of removing it.
Second, when the EAF becomes full, we propose to clear the EAF completely instead of removing an address in a FIFO manner.
With these changes, we can implement the EAF using a Bloom filter.
Doing so can reduce the storage overhead of EAF by 4x, to around 1.47% compared to the cache size.

## Slide 62: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 63: Large Working Set: 2 Cases
Cache
EAF
A
E
K
J
I
H
G
F
L
C
B
D
Cache
EAF
R
Q
P
O
N
M
L
S
J
I
H
G
F
E
D
K
C
B
A
1
2
Cache < Working set < Cache + EAF
Cache + EAF < Working Set
Notes: Thrashing happens when the working set is larger than the cache size. In the context of EAF, there are two cases. In the first case, the working set is larger than the cache but smaller than the blocks tracked by the cache and EAF together. In the second case, the working set is larger than the cache and EAF together. In both cases, the traditional LRU policy will lead to thrashing. I will discuss the operation of EAF in these two cases one by one.

## Slide 64: Large Working Set: Case 1
Cache
EAF
A
E
K
J
I
H
G
F
L
C
B
D


B
F
L
K
J
I
H
G
A
D
C
E
C
G
A
L
K
J
I
H
B
E
D
F

A
L
K
J
I
H
G
B
E
D
F
C












A
Sequence:
B
C
D
E
F
G
H
I
J
K
L
A
B
C
EAF Naive:
D

A
B
C
Cache < Working set < Cache + EAF
Notes: In the first case, the working set is smaller than the cache and EAF put together. Let us first look at how the original FIFO based implementation of EAF works.
Consider the following access sequence that accesses the blocks of the working set in a cyclic manner.
First, the access to block A misses in the cache. However, since the address is present in the EAF, it is inserted with a high priority into the cache.
The same thing happens with block B
and Block C after than.
In fact, every block in the access sequence will miss in the cache. As a result, the FIFO based implementation of EAF performs no better than traditional LRU.

## Slide 65: Large Working Set: Case 1
Cache
EAF
E
A
K
J
I
H
G
F
L
C
B
D
A
Sequence:
B
C
D
E
F
G
H
I
J
K
L
A
B
C
A
B
EAF BF:








A






EAF Naive:















A
L
K
J
I
H
G
B
E
D
C
A
B
F
A
L
K
J
I
H
G
B
E
D
F
C
A
B
D
H
G
B
E
D
F
C
A
A
L
K
J
I
B
C
D
D


Not removed
Not present in the EAF
Bloom-filter based EAF mitigates thrashing
H

G
F
E
I
Cache < Working set < Cache + EAF
Notes: Now lets look at how the Bloom-filter based EAF performs on this access sequence.
When block A is accessed, it misses in the cache but is present in the EAF. It is inserted with a high priority.
But unlike EAF-FIFO, the address is not removed from the EAF.
The same thing happens with Block B.
Moving forward, after the access to block D which also misses in the cache, the EAF becomes full.
At this point, the Bloom-filter based implementation will completely clear the EAF.
As a result, even though the next four accesses to E, F, G and H miss in the cache, their addresses will not be present in the EAF. Therefore, they will be inserted at the LRU position evicting only block I from the cache. As a result, 7 of the next 8 accesses will hit in the cache.
In fact, if the access sequence continues, the bloom-filter based implementation will periodically clear the EAF leading to cache hits to a fraction of the blocks.
So, the Bloom-filter based implementation of EAF mitigates caceh thrashing.

## Slide 66: Large Working Set: Case 2
Cache
EAF
R
Q
P
O
N
M
L
S
J
I
H
G
F
E
D
K
C
B
A
Problem: All blocks are predicted to have low reuse
Use Bimodal Insertion Policy for low reuse blocks. Insert few of them at the MRU position
Allow a fraction of the working set to stay in the cache
Cache + EAF < Working Set
Notes: Now lets move on to the second case of large working sets. In this case, since the working set is larger than both the cache and EAF together, none of the missed addresses will be present in the EAF.
As a result, all blocks will be predicted to have low reuse and inserted with low priority. If the cache is already filled with some other blocks, none of the blocks will get into the cache.
In this case, we would ideally like to allow a fraction of the working set to stay in the cache.
For this purpose, we propose to use the bimodal insertion policy for low reuse blocks. As a result, a few blocks of the working set will be inserted at the MRU position improving the cache utilization.

## Slide 67: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 68: EAF-Cache: Final Design
Cache
Bloom Filter
Counter
1
2
3
Cache eviction
Cache miss
Counter reaches max
Insert address into filter
Increment counter
Test if address is present in filter
Yes, insert at MRU. No, insert with BIP
Clear filter and counter
Notes: Lets take a look at the final design of our mechanism, the EAF-cache.
It augments the cache with a Bloom filter and a counter that keeps track of the number of addresses inserted into the Bloom filter.
On a cache eviction, the evicted address is inserted into the filter and the counter is incremented.
On a cache miss, if the missed block address is present in the Bloom filter, the block is inserted at the MRU position. Otherwise it is inserted with the bimodal insertion policy.
Finally, when the counter reaches a maximum, both the filter and the counter are cleared.

## Slide 69: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 70: EAF: Advantages
Cache
Bloom Filter
Counter
1. Simple to implement
2. Easy to design and verify
3. Works with other techniques (replacement policy)
Cache eviction
Cache miss
Notes: Apart from its ability to mitigate both pollution and thrashing, EAF has three other advantages.
First, it adds only a Bloom filter and a counter. Hardware implementations of the Bloom filter are well studied. So, EAF-cache is simple to implement.
Second, both the Bloom filter and the counter are outside the cache. As a result, our mechanism is easy to design and verify on top of existing cache implementations.
Finally, all operations on the EAF happen on a cache miss. As a result, EAF can work well with other techniques that monitor cache hits to improve performance, for example, the cache replacement policy.

## Slide 71: EAF: Disadvantage
Cache
A
First access
A
A
A
Second access
Miss
Problem: For an LRU-friendly application, EAF incurs one additional miss for most blocks
Dueling-EAF: set dueling between EAF and LRU
In EAF?
Notes: One limitation of the EAF is that when a high-reuse block is accessed for the first time, EAF will falsely predict the block to have low reuse and insert it at the LRU position. So the block will likely get evicted causing the second access to also be a cache miss.
Although this does not affect performance significantly for most applications, for LRU friendly applications, EAF incurs one additional miss for most blocks.
To mitigate this problem, we propose to use a previously proposed technique called set dueling to choose the best between the EAF and the LRU policies. Please read our paper for more details.

## Slide 72: Outline
Evicted-Address Filter
  Reuse Prediction
  Thrash Resistance
Final Design
Evaluation
Conclusion
Background and Motivation
Advantages and Disadvantages
Notes: Our mechanism has two components: a reuse prediction component and a thrash resistance component. I will describe both these components followed by the advantages and disadvantages of our proposed approach. Then, I will present our evaluation results and conclude.

## Slide 73: Methodology
Simulated System
  In-order cores, single issue, 4 GHz
  32 KB L1 cache, 256 KB L2 cache (private)
  Shared L3 cache (1MB to 16MB)
  Memory: 150 cycle row hit, 400 cycle row conflict
Benchmarks
  SPEC 2000, SPEC 2006, TPC-C, 3 TPC-H, Apache
Multi-programmed workloads
  Varying memory intensity and cache sensitivity
Metrics
  4 different metrics for performance and fairness
  Present weighted speedup

## Slide 74: Comparison with Prior Works
Addressing Cache Pollution
- No control on number of blocks inserted with high priority ⟹ Thrashing
Run-time Bypassing (RTB) – Johnson+ ISCA’97
- Memory region based reuse prediction
Single-usage Block Prediction (SU) – Piquet+ ACSAC’07
Signature-based Hit Prediction (SHIP) – Wu+ MICRO’11
- Program counter based reuse prediction
Miss Classification Table (MCT) – Collins+ MICRO’99
- One most recently evicted block
Notes: We compare EAF to five previous approaches.
Three of them address the cache pollution problem. Run time cache bypassing learns the reuse behavior of course grain memory regions to predict the reuse of individual cache blocks. Single usage block prediction and signature based hit prediction both use a program counter based reuse prediction mechanism, similar to the memory region approach. The miss classification table keeps track of one most recently evicted block to filter low-reuse blocks. The main drawback of these approaches is that they do not have inherent mechanism to control the number of high reuse blocks. As a result, when the working set is larger than the cache size, they will likely lead to thrashing.
The two other mechanisms we compare to address cache thrashing. They both use set dueling to identify applications with thrashing working sets and use the bimodal insertion policy for such applications. TA-DIP uses the traditional LRU replacement policy as the base policy and TA-DRRIP uses a different replacement policy called RRIP.

## Slide 75: Comparison with Prior Works
Addressing Cache Thrashing
- No mechanism to filter low-reuse blocks ⟹ Pollution
TA-DIP – Qureshi+ ISCA’07, Jaleel+ PACT’08
TA-DRRIP – Jaleel+ ISCA’10
- Use set dueling to determine thrashing applications
Notes: We compare EAF to five previous approaches.
Three of them address the cache pollution problem. Run time cache bypassing learns the reuse behavior of course grain memory regions to predict the reuse of individual cache blocks. Single usage block prediction and signature based hit prediction both use a program counter based reuse prediction mechanism, similar to the memory region approach. The miss classification table keeps track of one most recently evicted block to filter low-reuse blocks. The main drawback of these approaches is that they do not have inherent mechanism to control the number of high reuse blocks. As a result, when the working set is larger than the cache size, they will likely lead to thrashing.
The two other mechanisms we compare to address cache thrashing. They both use set dueling to identify applications with thrashing working sets and use the bimodal insertion policy for such applications. TA-DIP uses the traditional LRU replacement policy as the base policy and TA-DRRIP uses a different replacement policy called RRIP.

## Slide 76: Results – Summary
Chart: Performance Improvement over LRU
| 1-Core | 2-Core | 4-Core
TA-DIP | 0.01 | 0.04 | 0.02
TA-DRRIP | 0.05 | 0.08 | 0.11
RTB | 0.01 | 0.06 | 0.07
MCT | 0.01 | 0.1 | 0.06
SHIP | 0.04 | 0.1 | 0.13
EAF | 0.05 | 0.15 | 0.21
D-EAF | 0.07 | 0.15 | 0.205
Notes: This slide presents the summary of our performance results for systems with different number of cores.
As shown, our mechanisms outperform all prior approaches for all the three systems. Also, the multicore results are significantly better than the single core results. This is because, in a multicore system, pollution or thrashing caused by an application will affect useful blocks of other concurrently running applications.
SAY THAT LAST TWO BARS ARE EAF AND D-EAF

## Slide 77: 4-Core: Performance
Chart: Workload Number (135 workloads)
Notes: This figure compares the performance of EAF with the SHIP (BEST PREVIOUS MECHANISM) for all 4-core workloads. Each point on the x-axis corresponds to a 4-core workload and the workloads are sorted based on the performance improvements due to EAF. I would like to draw two conclusions. First, the average improvements of EAF is not due to few workloads. Rather, EAF outperforms SHIP for most workloads.
Second, EAF degrades performance for a few LRU-friendly workloads. However, Dueling-EAF mitigates this degradation while not significantly affecting the performance for other workloads.

## Slide 78: Effect of Cache Size
Chart: Weighted Speedup Improvement over LRU
| 1MB | 2MB | 4MB | 8MB | 2MB | 4MB | 8MB | 16MB | 2-Core | 4-Core
SHIP | 10 | 8 | 6 | 5 | 13 | 9 | 8 | 6
EAF | 15 | 10 | 8 | 6 | 21 | 15 | 11 | 7
D-EAF | 15 | 10 | 9 | 7 | 20.5 | 16 | 12 | 7
Notes: This figure shows the effect of varying the cache size on the performance of different schemes. As expected, the gap between different schemes decrease with increasing cache size. With larger cache sizes, the negative impact of pollution and thrashing also reduces.
However, our EAF-based approaches still provide better performance compared to both the LRU baseline and SHIP.

## Slide 79: Effect of EAF Size
Chart: # Addresses in EAF / # Blocks in Cache
| 0.0 | 0.2 | 0.4 | 0.600000000000001 | 0.8 | 1.0 | 1.2 | 1.4 | 1.6
1 Core | 1 | 2 | 2 | 4 | 5 | 5 | 5 | 4 | 4
2 Core | 10 | 11 | 13 | 14 | 15 | 15 | 15 | 15 | 15
4 Core | 12 | 15 | 18 | 19 | 20 | 21 | 21 | 20 | 20
Notes: Finally, let’s take a look at the effect of the number of addresses kept track in the EAF on its performance. The x-axis shows the ratio of the number of addresses in the EAF and the number of blocks in the cache.
When the number of addresses in the EAF is low, it falsely predicts many high reuse blocks as low reuse blocks.
On the other extreme, when the number of addresses in the EAF is high, it predicts too many blocks to have high reuse, more than what the cache can handle.
We find that having as many addresses in the EAF as there are blocks in the cache provides the best performance. Our paper describes the intuition behind this behavior.

## Slide 80: Other Results in Paper
EAF orthogonal to replacement policies
  LRU, RRIP – Jaleel+ ISCA’10
Performance improvement of EAF increases with increasing memory latency
EAF performs well on four different metrics
  Performance and fairness
Alternative EAF-based designs perform comparably
  Segmented EAF
  Decoupled-clear EAF
Notes: …

## Slide 81: Conclusion
Cache utilization is critical for system performance
  Pollution and thrashing degrade cache performance
  Prior works don’t address both problems concurrently
EAF-Cache
  Keep track of recently evicted block addresses in EAF
  Insert low reuse with low priority to mitigate pollution
  Clear EAF periodically and use BIP to mitigate thrashing
  Low complexity implementation using Bloom filter
EAF-Cache outperforms five prior approaches that address pollution or thrashing
Notes: …

## Slide 82: Base-Delta-Immediate Cache Compression
Gennady Pekhimenko, Vivek Seshadri, Onur Mutlu, Philip B. Gibbons, Michael A. Kozuch, and Todd C. Mowry, "Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches" Proceedings of the 21st ACM International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx)

## Slide 83: Executive Summary
Off-chip memory latency is high
  Large caches can help, but at significant cost
Compressing data in cache enables larger cache at low cost
Problem: Decompression is on the execution critical path
Goal: Design a new compression scheme that has
1. low decompression latency, 2. low cost, 3. high compression ratio
Observation: Many cache lines have low dynamic range data
Key Idea: Encode cachelines as a base + multiple differences
Solution: Base-Delta-Immediate compression with low decompression latency and high compression ratio
  Outperforms three state-of-the-art compression mechanisms

## Slide 84: Motivation for Cache Compression
Significant redundancy in data:
0x00000000
How can we exploit this redundancy?
  Cache compression helps
  Provides effect of a larger cache without making it physically larger
0x0000000B
0x00000003
0x00000004
…

## Slide 85: Background on Cache Compression
Key requirements:
  Fast (low decompression latency)
  Simple (avoid complex hardware changes)
  Effective (good compression ratio)
CPU
L2 Cache
Uncompressed
Compressed
Decompression
Uncompressed
L1 Cache
Hit

## Slide 86: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 

## Slide 87: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 

## Slide 88: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 
Frequent Pattern |  | / | 

## Slide 89: Shortcomings of Prior Work
Compression Mechanisms | Decompression Latency | Complexity | Compression Ratio
Zero |  |  | 
Frequent Value |  |  | 
Frequent Pattern |  | / | 
Our proposal: BΔI |  |  | 

## Slide 90: Outline
Motivation & Background
Key Idea & Our Mechanism
Evaluation
Conclusion

## Slide 91: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region

## Slide 92: How Common Are These Patterns?
Chart: Cache Coverage (%)
| libquantum | lbm | mcf | tpch17 | sjeng | omnetpp | tpch2 | sphinx3 | xalancbmk | bzip2 | tpch6 | leslie3d | apache | gromacs | astar | gobmk | soplex | gcc | hmmer | wrf | h264ref | zeusmp | cactusADM | GemsFDTD | Average
Zero | 1.2e-05 | 7e-06 | 0.008911 | 0.033323 | 0.032362 | 2.7e-05 | 0.065765 | 0.022031 | 0.000272 | 0.000176 | 0.12314 | 0.16955 | 0.072498 | 0.065675 | 0.016314 | 0.34373 | 0.26863 | 0.30068 | 0.003261 | 0.81434 | 0.00837 | 0.83736 | 0.66632 | 0.99428 | 0.20196
Repeated Values | 0.0001 | 6.5e-05 | 0.0001 | 0.000508 | 0.000146 | 0.0001 | 0.000529 | 0.008812 | 2e-06 | 0.036901 | 0.002005 | 0.095993 | 0.005072 | 0.010873 | 0.005914 | 0.020917 | 0.29969 | 0.038812 | 0.031345 | 0.083856 | 0.006414 | 0.13684 | 0.32178 | 0.001628 | 0.046184
Other Patterns | 0.000177 | 0.000138 | 0.060209 | 0.045394 | 0.070763 | 0.11701 | 0.075432 | 0.1168 | 0.21336 | 0.18863 | 0.12998 | 0.016265 | 0.23912 | 0.24082 | 0.42076 | 0.086109 | 0.18536 | 0.45647 | 0.84697 | 0.017818 | 0.91843 | 0.000306 | 0.000699 | 0.000345 | 0.18531
SPEC2006, databases, web workloads, 2MB L2 cache
“Other Patterns” include Narrow Values
  43% of the cache lines belong to key patterns

## Slide 93: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000FF
0x000000FF
0x000000FF
0x000000FF
…
0x00000000
0x0000000B
0x00000003
0x00000004
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region
  Low Dynamic Range:
  Differences between values are significantly smaller than the values themselves

## Slide 94: Key Idea: Base+Delta (B+Δ) Encoding
32-byte Uncompressed Cache Line
0xC04039C0
0xC04039C8
0xC04039D0
…
0xC04039F8
4 bytes
0xC04039C0
Base
0x00
1 byte
0x08
1 byte
0x10
1 byte
…
0x38
12-byte
Compressed Cache Line
  20 bytes saved
   Fast Decompression: vector addition
   Simple Hardware:
  arithmetic and comparison
   Effective: good compression ratio

## Slide 95: Can We Do Better?
Uncompressible cache line (with a single base):
Key idea:
Use more bases, e.g., two instead of one
Pro:
  More cache lines can be compressed
Cons:
  Unclear how to find these bases efficiently
  Higher overhead (due to additional bases)
0x00000000
0x09A40178
0x0000000B
0x09A4A838
…

## Slide 96: B+Δ with Multiple Arbitrary Bases
Chart: Compression Ratio
| GeoMean
1 | 1.3961
2 | 1.5113
3 | 1.4982
4 | 1.4326
8 | 1.3118
10 | 1.2742
16 | 1.2242
   2 bases – the best option based on evaluations

## Slide 97: How to Find Two Bases Efficiently?
  First base - first element in the cache line
  Second base - implicit base of 0
Advantages over 2 arbitrary bases:
  Better compression ratio
  Simpler compression logic
   Base+Delta part
   Immediate part
  Base-Delta-Immediate (BΔI) Compression

## Slide 98: B+Δ (with two arbitrary bases) vs. BΔI
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
B+Δ (2 bases) | 1.0625 | 1.0125 | 1.0254 | 1.1979 | 1.1332 | 1.375 | 1.7477 | 1.5346 | 1.3347 | 1.2446 | 1.5238 | 1.447 | 1.2608 | 1.4753 | 1.7447 | 1.3954 | 1.9793 | 1.7868 | 1.9739 | 1.9919 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5113
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
  Average compression ratio is close, but BΔI is simpler

## Slide 99: BΔI Implementation
Decompressor Design
  Low latency
Compressor Design
  Low cost and complexity
BΔI Cache Organization
  Modest complexity

## Slide 100: BΔI Decompressor Design
Δ0
B0
Δ1
Δ2
Δ3
Compressed Cache Line
V0
V1
V2
V3
+
+
Uncompressed Cache Line
+
+
B0
Δ0
B0
B0
B0
B0
Δ1
Δ2
Δ3
V0
V1
V2
V3
  Vector addition

## Slide 101: BΔI Compressor Design
32-byte Uncompressed Cache Line
8-byte B0
1-byte Δ
CU
8-byte B0
2-byte Δ
CU
8-byte B0
4-byte Δ
CU
4-byte B0
1-byte Δ
CU
4-byte B0
2-byte Δ
CU
2-byte B0
1-byte Δ
CU
Zero
CU
Rep.
Values
CU
Compression Selection Logic (based on compr. size)
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
CFlag &
CCL
Compression Flag & Compressed Cache Line
CFlag &
CCL
Compressed Cache Line

## Slide 102: BΔI Compression Unit: 8-byte B0 1-byte Δ
32-byte Uncompressed Cache Line
V0
V1
V2
V3
8 bytes
-
-
-
-
B0=
V0
V0
B0
B0
B0
B0
V0
V1
V2
V3
Δ0
Δ1
Δ2
Δ3
Within 1-byte range?
Within 1-byte range?
Within 1-byte range?
Within 1-byte range?
Is every element within 1-byte range?
Δ0
B0
Δ1
Δ2
Δ3
B0
Δ0
Δ1
Δ2
Δ3
Yes
No

## Slide 103: BΔI Cache Organization
Tag0
Tag1
…
…
…
…
Tag Storage:
Set0
Set1
Way0
Way1
Data0
…
…
Set0
Set1
Way0
Way1
…
Data1
…
32 bytes
Data Storage:
Conventional 2-way cache with 32-byte cache lines
BΔI: 4-way cache with 8-byte segmented data
Tag0
Tag1
…
…
…
…
Tag Storage:
Way0
Way1
Way2
Way3
…
…
Tag2
Tag3
…
…
Set0
Set1
Twice as many tags
C - Compr. encoding bits
C
Set0
Set1
…
…
…
…
…
…
…
…
S0
S0
S1
S2
S3
S4
S5
S6
S7
…
…
…
…
…
…
…
…
8 bytes
Tags map to multiple adjacent segments
2.3% overhead for 2 MB cache

## Slide 104: Qualitative Comparison with Prior Work
Zero-based designs
  ZCA [Dusser+, ICS’09]: zero-content augmented cache
  ZVC [Islam+, PACT’09]: zero-value cancelling
  Limited applicability (only zero values)
FVC [Yang+, MICRO’00]: frequent value compression
  High decompression latency and complexity
Pattern-based compression designs
  FPC [Alameldeen+, ISCA’04]: frequent pattern compression
    High decompression latency (5 cycles) and complexity
  C-pack [Chen+, T-VLSI Systems’10]: practical implementation of FPC-like algorithm
    High decompression latency (8 cycles)

## Slide 105: Outline
Motivation & Background
Key Idea & Our Mechanism
Evaluation
Conclusion

## Slide 106: Methodology
Simulator
  x86 event-driven simulator based on Simics [Magnusson+, Computer’02]
Workloads
  SPEC2006 benchmarks, TPC, Apache web server
  1 – 4 core simulations for 1 billion representative instructions
System Parameters
  L1/L2/L3 cache latencies from CACTI [Thoziyoor+, ISCA’08]
  4GHz, x86 in-order core, 512kB - 16MB L2, simple memory model (300-cycle latency for row-misses)

## Slide 107: Compression Ratio: BΔI vs. Prior Work
BΔI achieves the highest compression ratio
Chart: Compression Ratio
| lbm | wrf | hmmer | sphinx3 | tpch17 | libquantum | leslie3d | gromacs | sjeng | mcf | h264ref | tpch2 | omnetpp | apache | bzip2 | xalancbmk | astar | tpch6 | cactusADM | gcc | soplex | gobmk | zeusmp | GemsFDTD | GeoMean
ZCA | 1 | 1.0125 | 1.0002 | 1.0055 | 1.0288 | 1 | 1.1561 | 1.0914 | 1.0241 | 1 | 1.0005 | 1.1898 | 1 | 1.1083 | 1.0549 | 1 | 1.0013 | 1.2794 | 1.9738 | 1.5235 | 1.5406 | 1.801 | 1.9951 | 1.9966 | 1.2005
FVC | 1.0297 | 1.0125 | 1.0012 | 1.017 | 1.1457 | 1.4988 | 1.1857 | 1.1438 | 1.4157 | 1.3573 | 1.0143 | 1.4596 | 1.3574 | 1.3745 | 1.1968 | 1.3874 | 1.9381 | 1.7894 | 1.9738 | 1.9859 | 1.9598 | 1.9947 | 1.995 | 1.9966 | 1.4212
FPC | 1.004 | 1.0125 | 1.0225 | 1.0568 | 1.2307 | 1.3121 | 1.1774 | 1.4064 | 1.4705 | 1.5235 | 1.5442 | 1.5994 | 1.5763 | 1.7269 | 1.2651 | 1.6749 | 1.9072 | 1.9167 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5149
BΔI | 1.0039 | 1.0125 | 1.0257 | 1.1021 | 1.1832 | 1.3501 | 1.4052 | 1.4279 | 1.4975 | 1.5236 | 1.535 | 1.5416 | 1.5794 | 1.5993 | 1.6017 | 1.6112 | 1.7405 | 1.9257 | 1.9738 | 1.992 | 1.9922 | 1.9947 | 1.995 | 1.9966 | 1.5299
1.53
SPEC2006, databases, web workloads, 2MB L2

## Slide 108: Single-Core: IPC and MPKI
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 1.0859 | 1.1498 | 1.1819 | 1.2753 | 1.3788
BΔI | 1.0817 | 1.1425 | 1.2085 | 1.2401 | 1.346 | 1.4285
8.1%
5.2%
5.1%
4.9%
5.6%
3.6%
Chart: L2 cache size
| 512kB | 1MB | 2MB | 4MB | 8MB | 16MB
Baseline (no compr.) | 1 | 0.819 | 0.59143 | 0.46593 | 0.37544 | 0.27527
BΔI | 0.84292 | 0.62368 | 0.466 | 0.40552 | 0.30364 | 0.23666
16%
24%
21%
13%
19%
14%
BΔI achieves the performance of a 2X-size cache
Performance improves due to the decrease in MPKI

## Slide 109: Multi-Core Workloads
Application classification based on
  Compressibility: effective cache size increase
  (Low Compr. (LC) < 1.40, High Compr. (HC) >= 1.40)
  Sensitivity: performance gain with more cache
  (Low Sens. (LS) < 1.10, High Sens. (HS) >= 1.10; 512kB -> 2MB)
Three classes of applications:
  LCLS, HCLS, HCHS, no LCHS applications
For 2-core - random mixes of each possible class pairs (20 each, 120 total workloads)

## Slide 110: Multi-Core: Weighted Speedup
BΔI performance improvement is the highest (9.5%)
Chart: Normalized Weighted Speedup
| LCLS - LCLS | LCLS - HCLS | HCLS - HCLS | LCLS - HCHS | HCLS - HCHS | HCHS - HCHS | Low Sensitivity | High Sensitivity | GeoMean
ZCA | 1.0268 | 1.0154 | 1.0259 | 1.0182 | 1.1193 | 1.01 | 1.0353
FVC | 1.0277 | 1.0179 | 1.0345 | 1.0727 | 1.1468 | 1.08 | 1.0624
FPC | 1.0312 | 1.0197 | 1.0276 | 1.1 | 1.1495 | 1.176 | 1.0822
BΔI | 1.0446 | 1.0342 | 1.0431 | 1.1091 | 1.1651 | 1.18 | 1.0944
If at least one application is sensitive, then the performance improves

## Slide 111: Other Results in Paper
IPC comparison against upper bounds
  BΔI almost achieves performance of the 2X-size cache
Sensitivity study of having more than 2X tags
  Up to 1.98 average compression ratio
Effect on bandwidth consumption
  2.31X decrease on average
Detailed quantitative comparison with prior work
Cost analysis of the proposed changes
  2.3% L2 cache area increase

## Slide 112: Conclusion
A new Base-Delta-Immediate compression mechanism
Key insight: many cache lines can be efficiently represented using base + delta encoding
Key properties:
  Low latency decompression
  Simple hardware implementation
  High compression ratio with high coverage
Improves cache hit ratio and performance of both single-core and multi-core workloads
  Outperforms state-of-the-art cache compression techniques: FVC and FPC

## Slide 113: Linearly Compressed Pages
Gennady Pekhimenko, Vivek Seshadri, Yoongu Kim, Hongyi Xin, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency" SAFARI Technical Report, TR-SAFARI-2012-005, Carnegie Mellon University, September 2012.

## Slide 114: Executive Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Idea: Compress data in main memory
Problem: How to avoid latency increase?
Solution: Linearly Compressed Pages (LCP):
fixed-size cache line granularity compression
1. Increases capacity (69% on average)
2. Decreases bandwidth consumption (46%)
3. Improves overall performance (9.5%)

## Slide 115: Challenges in Main Memory Compression
Address Computation
Mapping and Fragmentation
Physically Tagged Caches

## Slide 116: Address Computation
L0
L1
L2
. . .
LN-1
Cache Line (64B)
Address Offset
0
64
128
(N-1)*64
L0
L1
L2
. . .
LN-1
Compressed Page
0
?
?
?
Address Offset
Uncompressed Page

## Slide 117: Mapping and Fragmentation
Virtual Page
(4kB)
Physical Page
(? kB)
Fragmentation
Virtual
Address
Physical
Address

## Slide 118: Physically Tagged Caches
Core
TLB
tag
tag
tag
Physical Address
data
data
data
Virtual
Address
Critical Path
Address Translation
L2 Cache
Lines

## Slide 119: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 

## Slide 120: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 

## Slide 121: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 
LCP: Our Proposal |  |  |  | 

## Slide 122: Linearly Compressed Pages (LCP): Key Idea
64B
64B
64B
64B
. . .
. . .
M
E
Metadata (64B):
? (compressible)
Exception
Storage
4:1 Compression
64B
Uncompressed Page (4kB: 64*64B)
Compressed Data
(1kB)

## Slide 123: LCP Overview
Page Table entry extension
  compression type and size
  extended physical base address
Operating System management support
  4 memory pools (512B, 1kB, 2kB, 4kB)
Changes to cache tagging logic
  physical page base address + cache line index
  (within a page)
Handling page overflows
Compression algorithms: BDI [PACT’12] , FPC [ISCA’04]

## Slide 124: LCP Optimizations
Metadata cache
  Avoids additional requests to metadata
Memory bandwidth reduction:
Zero pages and zero cache lines
  Handled separately in TLB (1-bit) and in metadata
  (1-bit per cache line)
Integration with cache compression
  BDI and FPC
64B
64B
64B
64B
1 transfer
instead of 4

## Slide 125: Methodology
Simulator
  x86 event-driven simulators
    Simics-based [Magnusson+, Computer’02] for CPU
    Multi2Sim [Ubal+, PACT’12] for GPU
Workloads
  SPEC2006 benchmarks, TPC, Apache web server, GPGPU applications
System Parameters
  L1/L2/L3 cache latencies from CACTI [Thoziyoor+, ISCA’08]
  512kB - 16MB L2, simple memory model

## Slide 126: Compression Ratio Comparison
Chart: GeoMean
| GeoMean
Zero Page | 1.2982
FPC | 1.5908
LCP (BDI) | 1.6239
LCP (BDI+FPC-fixed) | 1.6909
MXT | 2.3051
LZ | 2.6049
SPEC2006, databases, web workloads, 2MB L2 cache
LCP-based frameworks achieve competitive average compression ratios with prior work

## Slide 127: Bandwidth Consumption Decrease
SPEC2006, databases, web workloads, 2MB L2 cache
Chart: Normalized BPKI
| GeoMean
FPC-cache | 0.92005
BDI-cache | 0.89057
FPC-memory | 0.57215
(None, LCP-BDI) | 0.62549
(FPC, FPC) | 0.5362
(BDI, LCP-BDI) | 0.55124
(BDI, LCP-BDI+FPC-fixed) | 0.53836
LCP frameworks significantly reduce bandwidth (46%)
Better
Notes: BPKI – bandwidth per kilo instruction – lower means better.

## Slide 128: Performance Improvement
Cores | LCP-BDI | (BDI, LCP-BDI) | (BDI, LCP-BDI+FPC-fixed)
1 | 6.1% | 9.5% | 9.3%
2 | 13.9% | 23.7% | 23.6%
4 | 10.7% | 22.6% | 22.5%
LCP frameworks significantly improve performance

## Slide 129: Conclusion
A new main memory compression framework called LCP (Linearly Compressed Pages)
  Key idea: ﬁxed size for compressed cache lines within a page and fixed compression algorithm per page
LCP evaluation:
  Increases capacity (69% on average)
  Decreases bandwidth consumption (46%)
  Improves overall performance (9.5%)
  Decreases energy of the off-chip bus (37%)

## Slide 130: Controlled Shared Caching

## Slide 131: Controlled Cache Sharing
Utility based cache partitioning
  Qureshi and Patt, “Utility-Based Cache Partitioning: A Low-Overhead, High-Performance, Runtime Mechanism to Partition Shared Caches,” MICRO 2006.
  Suh et al., “A New Memory Monitoring Scheme for Memory-Aware Scheduling and Partitioning,” HPCA 2002.
Fair cache partitioning
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.
Shared/private mixed cache mechanisms
  Qureshi, “Adaptive Spill-Receive for Robust High-Performance Caching in CMPs,” HPCA 2009.
  Hardavellas et al., “Reactive NUCA: Near-Optimal Block Placement and Replication in Distributed Caches,” ISCA 2009.

## Slide 132: Utility Based Shared Cache Partitioning
Goal: Maximize system throughput
Observation: Not all threads/applications benefit equally from caching  simple LRU replacement not good for system throughput
Idea: Allocate more cache space to applications that obtain the most benefit from more space
The high-level idea can be applied to other shared resources as well.
Qureshi and Patt, “Utility-Based Cache Partitioning: A Low-Overhead, High-Performance, Runtime Mechanism to Partition Shared Caches,” MICRO 2006.
Suh et al., “A New Memory Monitoring Scheme for Memory-Aware Scheduling and Partitioning,” HPCA 2002.

## Slide 133: Marginal Utility of a Cache Way
Utility Uab = Misses with a ways – Misses with b ways
Low Utility
High Utility
Saturating Utility
Num ways from 16-way 1MB L2
Misses per 1000 instructions

## Slide 134: Utility Based Shared Cache Partitioning Motivation
Num ways from 16-way 1MB L2
Misses per 1000 instructions (MPKI)
equake
vpr
LRU
UTIL
Improve performance by giving more cache to the application that benefits more from cache

## Slide 135: Utility Based Cache Partitioning (III)
Three components:
Utility Monitors (UMON) per core
Partitioning Algorithm (PA)
Replacement support to enforce partitions
I$
D$
Core1
I$
D$
Core2
Shared
L2 cache
Main Memory
UMON1
UMON2
PA

## Slide 136: Utility Monitors
For each core, simulate LRU policy using ATD
Hit counters in ATD to count hits per recency position
LRU is a stack algorithm: hit counts  utility E.g. hits(2 ways) = H0+H1
MTD
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
ATD
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
+
+
+
+
(MRU)H0 H1 H2…H15(LRU)

## Slide 137: Utility Monitors

## Slide 138: Dynamic Set Sampling
Extra tags incur hardware and power overhead
Dynamic Set Sampling reduces overhead [Qureshi, ISCA’06]
32 sets sufficient (analytical bounds)
Storage < 2kB/UMON
MTD
ATD
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
+
+
+
+
(MRU)H0 H1 H2…H15(LRU)
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
Set B
Set E
Set G
Set A
Set C
Set D
Set F
Set H
Set B
Set E
Set G
UMON (DSS)

## Slide 139: Partitioning Algorithm
Evaluate all possible partitions and select the best
With a ways to core1 and (16-a) ways to core2:
Hitscore1 = (H0 + H1 + … + Ha-1) ---- from UMON1 Hitscore2 = (H0 + H1 + … + H16-a-1) ---- from UMON2
Select a that maximizes (Hitscore1 + Hitscore2)
Partitioning done once every 5 million cycles

## Slide 140: Way Partitioning
Way partitioning support: [Suh+ HPCA’02, Iyer ICS’04]
  Each line has core-id bits
  On a miss, count ways_occupied in set by miss-causing app
ways_occupied < ways_given
Yes
No
Victim is the LRU line from other app
Victim is the LRU line from miss-causing app

## Slide 141: Performance Metrics
Three metrics for performance:
Weighted Speedup (default metric)  perf = IPC1/SingleIPC1 + IPC2/SingleIPC2  correlates with reduction in execution time
Throughput  perf = IPC1 + IPC2  can be unfair to low-IPC application
Hmean-fairness  perf = hmean(IPC1/SingleIPC1, IPC2/SingleIPC2)  balances fairness and performance

## Slide 142: Weighted Speedup Results for UCP

## Slide 143: IPC Results for UCP
UCP improves average throughput by 17%

## Slide 144: Any Problems with UCP So Far?
- Scalability
- Non-convex curves?
Time complexity of partitioning low for two cores (number of possible partitions ≈ number of ways)
Possible partitions increase exponentially with cores
For a 32-way cache, possible partitions:
  4 cores  6545
  8 cores  15.4 million
Problem NP hard  need scalable partitioning algorithm

## Slide 145: Greedy Algorithm [Stone+ ToC ’92]
GA allocates 1 block to the app that has the max utility for one block. Repeat till all blocks allocated
Optimal partitioning when utility curves are convex
Pathological behavior for non-convex curves

## Slide 146: Problem with Greedy Algorithm
Problem: GA considers benefit only from the immediate block. Hence, it fails to exploit large gains from looking ahead
In each iteration, the utility for 1 block:
U(A) = 10 misses U(B) = 0 misses
Blocks assigned
Misses
All blocks assigned to A, even if B has same miss reduction with fewer blocks

## Slide 147: Lookahead Algorithm
Marginal Utility (MU) = Utility per cache resource
  MUab = Uab/(b-a)
GA considers MU for 1 block. LA considers MU for all possible allocations
Select the app that has the max value for MU. Allocate it as many blocks required to get max MU
Repeat till all blocks assigned

## Slide 148: Lookahead Algorithm Example
  Time complexity ≈ ways2/2 (512 ops for 32-ways)
Iteration 1:
MU(A) = 10/1 block MU(B) = 80/3 blocks
B gets 3 blocks
Result: A gets 5 blocks and B gets 3 blocks (Optimal)
Next five iterations:
MU(A) = 10/1 block
MU(B) = 0
A gets 1 block
Blocks assigned
Misses

## Slide 149: UCP Results
Four cores sharing a 2MB 32-way L2
Mix2
(swm-glg-mesa-prl)
Mix3
(mcf-applu-art-vrtx)
Mix4
(mcf-art-eqk-wupw)
Mix1
(gap-applu-apsi-gzp)
LA performs similar to EvalAll, with low time-complexity
LRU
UCP(Greedy)
UCP(Lookahead)
UCP(EvalAll)

## Slide 150: Utility Based Cache Partitioning
Advantages over LRU
  + Improves system throughput
  + Better utilizes the shared cache
Disadvantages
  - Fairness, QoS?
Limitations
  - Scalability: Partitioning limited to ways. What if you have numWays < numApps?
  - Scalability: How is utility computed in a distributed cache?
  - What if past behavior is not a good predictor of utility?

## Slide 151: Fair Shared Cache Partitioning
Goal: Equalize the slowdowns of multiple threads sharing the cache
Idea: Dynamically estimate slowdowns due to sharing and assign cache blocks to balance slowdowns
Approximate slowdown with change in miss rate
+ Simple
- Not accurate. Why?
  Kim et al., “Fair Cache Sharing and Partitioning in a Chip Multiprocessor Architecture,” PACT 2004.

## Slide 152: Problem with Shared Caches
L2 $
L1 $
……
Processor Core 1
L1 $
Processor Core 2
←t1

## Slide 153: Problem with Shared Caches
L1 $
Processor Core 1
L1 $
Processor Core 2
L2 $
……
t2→

## Slide 154: Problem with Shared Caches
L1 $
L2 $
……
Processor Core 1
Processor Core 2
←t1
L1 $
t2→
t2’s throughput is significantly reduced due to unfair cache sharing.

## Slide 155: Problem with Shared Caches

## Slide 156: Fairness Metrics
Uniform slowdown
Minimize:
  Ideally:

## Slide 157: Block-Granularity Partitioning
LRU
LRU
LRU
LRU
P1: 448B
P2 Miss
P2: 576B
Current Partition
P1: 384B
P2: 640B
Target Partition
Modified LRU cache replacement policy
  G. Suh, et. al., HPCA 2002

## Slide 158: Block-Granularity Partitioning
LRU
LRU
LRU
*
LRU
P1: 448B
P2 Miss
P2: 576B
Current Partition
P1: 384B
P2: 640B
Target Partition
Modified LRU cache replacement policy
  G. Suh, et. al., HPCA 2002
LRU
LRU
LRU
*
LRU
P1: 384B
P2: 640B
Current Partition
P1: 384B
P2: 640B
Target Partition

## Slide 159: Dynamic Fair Caching Algorithm
P1:
P2:
Ex) Optimizing
M3 metric
P1:
P2:
Target Partition
MissRate alone
P1:
P2:
MissRate shared
Repartitioning
interval

## Slide 160: Dynamic Fair Caching Algorithm
1st Interval
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:
P2:
MissRate shared
P1:20%
P2:15%
MissRate shared
P1:256KB
P2:256KB
Target Partition
Notes: At the very beginning, the static profiling obtained miss rate of 20% for P1 and 5% for P2.
Initially, target partitions are equal to P1 and P2.
After the 1st interval, we get shared miss rate by dynamic profiling and it has 20% and 15% miss rate.

## Slide 161: Dynamic Fair Caching Algorithm
Repartition!
Evaluate M3
P1: 20% / 20%
P2: 15% / 5%
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:15%
MissRate shared
P1:256KB
P2:256KB
Target Partition
P1:192KB
P2:320KB
Target Partition
Partition granularity: 64KB
Notes: At repartitioning, we evaluate M3. It equalize the increase in miss rate. P1 has no increase while P2 has 3 times increase.
In this case, we increase partition size for P2. We used 64KB partition granularity.

## Slide 162: Dynamic Fair Caching Algorithm
2nd Interval
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:15%
MissRate shared
P1:20%
P2:15%
MissRate shared
P1:20%
P2:10%
MissRate shared
P1:192KB
P2:320KB
Target Partition
Notes: In second interval, new target partition is applied. After the execution, we get new shared miss rate. same 20% and 10%. We have 5% reduction in miss rate.

## Slide 163: Dynamic Fair Caching Algorithm
Repartition!
Evaluate M3
P1: 20% / 20%
P2: 10% / 5%
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:15%
MissRate shared
P1:20%
P2:10%
MissRate shared
P1:192KB
P2:320KB
Target Partition
P1:128KB
P2:384KB
Target Partition
Notes: When we evaluate M3, again P2 requires more cache space. So we increase it.

## Slide 164: Dynamic Fair Caching Algorithm
3rd Interval
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:10%
MissRate shared
P1:128KB
P2:384KB
Target Partition
P1:20%
P2:10%
MissRate shared
P1:25%
P2: 9%
MissRate shared
Notes: After third interval, dynamic profiling get the miss rate for P1 25% and 9% for P2.

## Slide 165: Dynamic Fair Caching Algorithm
Repartition!
Do Rollback if:
P2: Δ<Trollback
Δ=MRold-MRnew
P1:20%
P2: 5%
MissRate alone
Repartitioning
interval
P1:20%
P2:10%
MissRate shared
P1:25%
P2: 9%
MissRate shared
P1:128KB
P2:384KB
Target Partition
P1:192KB
P2:320KB
Target Partition
Notes: There is a hidden step of rollback phase.
In this step, we check whether P2’s miss rate is reduced more than rollback threshold.
Because we increased cache partition, we expected to see reduction in miss rate.
In our example, P2 only reduced 1% miss rate which is smaller than rollback threshold.
So, we cancel our previous decision and go back to the previous partition.

## Slide 166: Dynamic Fair Caching Results
Improves both fairness and throughput

## Slide 167: Effect of Partitioning Interval
Fine-grained partitioning is important for both fairness and throughput

## Slide 168: Benefits of Fair Caching
Problems of unfair cache sharing
  Sub-optimal throughput
  Thread starvation
  Priority inversion
  Thread-mix dependent performance
Benefits of fair caching
  Better fairness
  Better throughput
  Fair caching likely simplifies OS scheduler design

## Slide 169: Advantages/Disadvantages of the Approach
Advantages
  + No (reduced) starvation
  + Better average throughput
Disadvantages
  - Scalable to many cores?
  - Is this the best (or a good) fairness metric?
  - Does this provide performance isolation in cache?
  - Alone miss rate estimation can be incorrect (estimation interval different from enforcement interval)

## Slide 170: Software-Based Shared Cache Management
Assume no hardware support (demand based cache sharing, i.e. LRU replacement)
How can the OS best utilize the cache?
Cache sharing aware thread scheduling
  Schedule workloads that “play nicely” together in the cache
    E.g., working sets together fit in the cache
    Requires static/dynamic profiling of application behavior
    Fedorova et al., “Improving Performance Isolation on Chip Multiprocessors via an Operating System Scheduler,” PACT 2007.
Cache sharing aware page coloring
  Dynamically monitor miss rate over an interval and change virtual to physical mapping to minimize miss rate
    Try out different partitions

## Slide 171: OS Based Cache Partitioning
Lin et al., “Gaining Insights into Multi-Core Cache Partitioning: Bridging the Gap between Simulation and Real Systems,” HPCA 2008.
Cho and Jin, “Managing Distributed, Shared L2 Caches through OS-Level Page Allocation,” MICRO 2006.
Static cache partitioning
  Predetermines the amount of cache blocks allocated to each program at the beginning of its execution
  Divides shared cache to multiple regions and partitions cache regions through OS page address mapping
Dynamic cache partitioning
  Adjusts cache quota among processes dynamically
  Page re-coloring
  Dynamically changes processes’ cache usage through OS page address re-mapping

## Slide 172: Page Coloring
Physical memory divided into colors
Colors map to different cache sets
Cache partitioning
  Ensure two threads are allocated
  pages of different colors
Thread A
Thread B
Cache
Way-1
Way-n
…………
Memory page

## Slide 173: Page Coloring
virtual page number
Virtual address
page offset
physical page number
Physical address
Page offset
Address translation
Cache tag
Block offset
Set index
Cache address
Physically indexed cache
page color bits
… …
OS control
=
Physically indexed caches are divided into multiple regions (colors).
All cache lines in a physical page are cached in one of those regions (colors).
OS can control the page color of a virtual page through address mapping
(by selecting a physical page with a specific value in its page color bits).
Notes: Let me introduce page coloring technique first.
1. A virtual address can be divide into two parts: Virtual page number and page offset
(In our experimental system, the page size is 4KB, so length of page offset bits are 12)
2. The virtual address is converted to physical address by address translation controlled by OS.
Virtual page number is mapped to a physical page number and page offset remain same.
3. The physical address is used in a physically indexed cache. The cache address is divided into tag, set index and block offset.
4. The common bits between physical page number and set index are referred as page color bits.
5. The physically indexed cache is then divided into multiple regions. Each OS page will cached in one of those regions. Indexed by the page color.
In a summary, 1) 2)…

## Slide 174: Static Cache Partitioning using Page Coloring
… …
...
……
…
……
…
Physically indexed cache
…
……
……
…
Physical pages are grouped to page bins
according to their page color
1
2
3
4
…
i+2
i
i+1
…
Process 1
1
2
3
4
…
i+2
i
i+1
…
Process 2
OS address mapping
Shared cache is partitioned between two processes through address mapping.
Cost: Main memory space needs to be partitioned, too.
Notes: 1. This slide shows an example how we enhance page coloring to partition shared cache between two processes.
2. Physical pages are grouped into page bins according to their page color. The pages in a same bin will be cached in same cache region or cache color in a physically indexed cache.
3. Suppose there are two processes running on a dual-core processor. Each processor has a set of pages need to be mapped to physical pages.
4. If we limit that pages from one process can only be mapped to a subset of page bins. Then pages from a process will only use part of the cache.
In a summary,
… We call this restriction co-partitioning.

## Slide 175: Dynamic Cache Partitioning via Page Re-Coloring
Allocated color
page color table
……
N - 1
0
1
2
3
Page re-coloring:
  Allocate page in new color
  Copy memory contents
  Free old page
Allocated colors
Pages of a process are organized into linked lists by their colors.
Memory allocation guarantees that pages are evenly distributed into all the lists (colors) to avoid hot points.
Notes: This slides show how we mange the pages and how we design the dynamic cache partitioning.
1. We link all the pages allocated to a process by their page colors. A page links table is added to each working process. And Memory allocation guarantees that pages are evenly distributed into all the cache colors to avoid hot points. 2. Suppose at the beginning of execution, 3 colors was assigned to the process: red, green and yellow. Pages are allocated in a round-robin fashion among those 3 colors.
3. If a policy decide to expand number of colors from 3 to 4, for example, the blue color is allocated to the process
4. one of every 4 pages are selected for migration. And we re-coloring those pages to the new color.
The re-coloring procedure includes three steps:
1. Allocate a physical page in new color
2. Copy memory contents from old page to new page
3. Free old page.
We execute these three steps for all pages that need to be re-colored.

## Slide 176: Dynamic Partitioning in Dual Core
Init: Partition the cache as (8:8)
Run current partition (P0:P1) for one epoch
finished
Try one epoch for each of the two neighboring
partitions: (P0 – 1: P1+1) and (P0 + 1: P1-1)
Choose next partitioning with best policy
metrics measurement (e.g., cache miss rate)
No
Yes
Exit
Notes: Next, I will present a simple dynamic partition policy we used for performance.
1. Initially, half cache capacity is allocated to each program.
2. We then enter the loops of trying to find optimal partitioning regarding a policy metrics M.
3. We first run one period for current partitioning, then try one period for each of the two neighboring partitionings.
4. We choosing best partition for the next epoch based on their policy metrics measurement.
We repeat this loop until the completion of the workload.
This is a simple greedy policy which emulate the policy of a HPCA’02 paper

## Slide 177: Experimental Environment
Dell PowerEdge1950
  Two-way SMP, Intel dual-core Xeon 5160
  Shared 4MB L2 cache, 16-way
  8GB Fully Buffered DIMM
Red Hat Enterprise Linux 4.0
  2.6.20.3 kernel
  Performance counter tools from HP (Pfmon)
  Divide L2 cache into 16 colors
Notes: We conducted our experiment on a two-way SMP machine that has two intel dual-core Xeon processors. Each processor has a 4MB 16-way L2 cache shared by two processor cores. The machine has 4 2GB Fully buffered DIMM as main memory.
We install RHEL 4.0 on the machine and use 2.6 kernel and patched the kernel with hardware Performance counter tools from HP.
And we extend linux kernel to support both static and dynamic cache partitioning. The L2 cache is divided into 16 colors.

## Slide 178: Performance – Static & Dynamic
Aim to minimize combined miss rate
For RG-type, and some RY-type:
  Static partitioning outperforms dynamic partitioning
For RR- and RY-type, and some RY-type
  Dynamic partitioning outperforms static partitioning
Notes: This figures shows the comparison between the performance of best static partitioning and the performance by the dynamic partitioning policies, using combined miss rates as policy metrics.
It is worth noting that we assume full profiling information is available for the static partitioning. Without such profiling information, the dynamic partitioning perform comparable with static partitioning.
If we look into the workload individually, some workloads perform better by static partitioning
while some other workload performance better by dynamic partitioning.

## Slide 179: Software vs. Hardware Cache Management
Software advantages
  + No need to change hardware
  + Easier to upgrade/change algorithm (not burned into hardware)
Disadvantages
  - Less flexible: large granularity (page-based instead of way/block)
  - Limited page colors  reduced performance per application (limited physical memory space!), reduced flexibility
  - Changing partition size has high overhead  page mapping changes
  - Adaptivity is slow: hardware can adapt every cycle (possibly)
  - Not enough information exposed to software (e.g., number of misses due to inter-thread conflict)

## Slide 180: Private/Shared Caching
Example: Adaptive spill/receive caching
Goal: Achieve the benefits of private caches (low latency, performance isolation) while sharing cache capacity across cores
Idea: Start with a private cache design (for performance isolation), but dynamically steal space from other cores that do not need all their private caches
  Some caches can spill their data to other cores’ caches dynamically
Qureshi, “Adaptive Spill-Receive for Robust High-Performance Caching in CMPs,” HPCA 2009.

## Slide 181: Revisiting Private Caches on CMP
Private caches avoid the need for shared interconnect
++ fast latency, tiled design, performance isolation
Core A
I$
D$
CACHE A
Core B
I$
D$
CACHE B
Core C
I$
D$
CACHE C
Core D
I$
D$
CACHE D
Memory
Problem: When one core needs more cache and other core
has spare cache, private-cache CMPs cannot share capacity

## Slide 182: Cache Line Spilling
Spill evicted line from one cache to neighbor cache
- Co-operative caching (CC) [ Chang+ ISCA’06]
Problem with CC:
Performance depends on the parameter (spill probability)
All caches spill as well as receive  Limited improvement
Cache A
Cache B
Cache C
Cache D
Spill
Goal: Robust High-Performance Capacity Sharing with Negligible Overhead

## Slide 183: Spill-Receive Architecture
Each Cache is either a Spiller or Receiver but not both
- Lines from spiller cache are spilled to one of the receivers
- Evicted lines from receiver cache are discarded
What is the best N-bit binary string that maximizes the performance of Spill Receive Architecture  Dynamic Spill Receive (DSR)
Cache A
Cache B
Cache C
Cache D
Spill
S/R =1
(Spiller cache)
S/R =0
(Receiver cache)
S/R =1
(Spiller cache)
S/R =0
(Receiver cache)

## Slide 184: Dynamic Spill-Receive via “Set Dueling”
Spiller-sets
Follower Sets
Receiver-sets
    Divide the cache in three:
      Spiller sets
      Receiver sets
      Follower sets (winner of spiller, receiver)
    n-bit PSEL counter
    misses to spiller-sets: PSEL--
    misses to receiver-set: PSEL++
    MSB of PSEL decides policy for Follower sets:
      MSB = 0, Use spill
      MSB = 1, Use receive
PSEL
-
miss
+
miss
MSB = 0?
YES
No
Use Recv
Use spill
monitor  choose  apply
(using a single counter)

## Slide 185: Dynamic Spill-Receive Architecture
Cache A
Cache B
Cache C
Cache D
Set X
Set Y
AlwaysSpill
AlwaysRecv
-
+
Miss in Set X
in any cache
Miss in Set Y
in any cache
PSEL B
PSEL C
PSEL D
PSEL A
Decides policy for all sets of Cache A (except X and Y)
Each cache learns whether it should act as a spiller or receiver

## Slide 186: Experimental Setup
  Baseline Study:
    4-core CMP with in-order cores
    Private Cache Hierarchy: 16KB L1, 1MB L2
    10 cycle latency for local hits, 40 cycles for remote hits
  Benchmarks:
    6 benchmarks that have extra cache: “Givers” (G)
    6 benchmarks that benefit from more cache: “Takers” (T)
    All 4-thread combinations of 12 benchmarks: 495 total
    Five types of workloads:
G4T0
G3T1
G2T2
G1T3
G0T4

## Slide 187: Results for Throughput
On average, DSR improves throughput by 18%, co-operative caching by 7%
DSR provides 90% of the benefit of knowing the best decisions a priori
* DSR implemented with 32 dedicated sets and 10 bit PSEL counters

## Slide 188: Results for Weighted Speedup
On average, DSR improves weighted speedup by 13%

## Slide 189: Results for Hmean Speedup
On average, DSR improves Hmean Fairness from 0.58 to 0.78

## Slide 190: DSR vs. Faster Shared Cache
DSR (with 40 cycle extra for remote hits) performs similar to shared cache with zero latency overhead and crossbar interconnect

## Slide 191: Scalability of DSR
DSR improves average throughput by 19% for both systems
(No performance degradation for any of the workloads)

## Slide 192: Quality of Service with DSR
Over time, ΔMiss 0, if DSR is causing more misses.
For 1 % of the 495x4 =1980 apps, DSR causes IPC loss of > 5%
In some cases, important to ensure that performance does not degrade compared to dedicated private cache  QoS
DSR can ensure QoS: change PSEL counters by weight of miss:
ΔMiss = MissesWithDSR – MissesWithNoSpill
Weight of Miss = 1 + Max(0, f(ΔMiss))
Calculate weight every 4M cycles. Needs 3 counters per core
Estimated by Spiller Sets

## Slide 193: IPC of QoS-Aware DSR
IPC curves for other categories almost overlap for the two schemes.
Avg. throughput improvement across all 495 workloads similar (17.5% vs. 18%)
For Category: G0T4
IPC Normalized To NoSpill

## Slide 194: Distributed Caches

## Slide 195: Caching for Parallel Applications
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
Data placement determines performance
Goal: place data on chip close to where they are used
cache
slice

## Slide 196: Shared Cache Management: Research Topics
Scalable partitioning algorithms
  Distributed caches have different tradeoffs
Configurable partitioning algorithms
  Many metrics may need to be optimized at different times or at the same time
  It is not only about overall performance
Ability to have high capacity AND high locality (fast access)
Within vs. across-application prioritization
Holistic design
  How to manage caches, NoC, and memory controllers together?
Cache coherence in shared/private distributed caches

## Slide 197: Scalable Many-Core Memory Systems Topic 4: Cache Management
Prof. Onur Mutlu
http://www.ece.cmu.edu/~omutlu
onur@cmu.edu
HiPEAC ACACES Summer School 2013
July 15-19, 2013