## Slide 1: Scalable Many-Core Memory Systems Optional Topic 5: Interconnects
Prof. Onur Mutlu
http://www.ece.cmu.edu/~omutlu
onur@cmu.edu
HiPEAC ACACES Summer School 2013
July 15-19, 2013

## Slide 2: What Will You Learn in This Course?
Scalable Many-Core Memory Systems
  July 15-19, 2013
Topic 1: Main memory basics, DRAM scaling
Topic 2: Emerging memory technologies and hybrid memories
Topic 3: Main memory interference and QoS
Topic 4 (unlikely): Cache management
Topic 5 (unlikely): Interconnects
Major Overview Reading:
  Mutlu, “Memory Scaling: A Systems Architecture Perspective,” IMW 2013.

## Slide 3: Readings and Videos

## Slide 4: Readings for Topic 5
Required – Interconnects in Multi-Core
  Moscibroda and Mutlu, “A Case for Bufferless Routing in On-Chip Networks,” ISCA 2009.
  Fallin et al., “CHIPPER: A Low-Complexity Bufferless Deflection Router,” HPCA 2011.
  Fallin et al., “MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect,” NOCS 2012.
  Das et al., “Application-Aware Prioritization Mechanisms for On-Chip Networks,” MICRO 2009.
  Das et al., “Aergia: Exploiting Packet Latency Slack in On-Chip Networks,” ISCA 2010, IEEE Micro 2011.
Recommended
  Grot et al. “Preemptive Virtual Clock: A Flexible, Efficient, and Cost-effective QOS Scheme for Networks-on-Chip,” MICRO 2009.
  Grot et al., “Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees,” ISCA 2011, IEEE Micro 2012.

## Slide 5: More Readings for Topic 5
Studies of congestion and congestion control in on-chip vs. internet-like networks
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)
George Nychis, Chris Fallin, Thomas Moscibroda, and Onur Mutlu, "Next Generation On-Chip Networks: What Kind of Congestion Control Do We Need?" Proceedings of the 9th ACM Workshop on Hot Topics in Networks (HOTNETS), Monterey, CA, October 2010. Slides (ppt) (key)

## Slide 6: Videos for Topic 5
Interconnects
  http://www.youtube.com/watch?v=6xEpbFVgnf8&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=33
GPUs and SIMD processing
  Vector/array processing basics: http://www.youtube.com/watch?v=f-XL4BNRoBA&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=15
  GPUs versus other execution models: http://www.youtube.com/watch?v=dl5TZ4-oao0&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=19
  GPUs in more detail: http://www.youtube.com/watch?v=vr5hbSkb1Eg&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=20

## Slide 7: Readings for Prefetching
Prefetching
  Srinath et al., “Feedback Directed Prefetching: Improving the Performance and Bandwidth-Efficiency of Hardware Prefetchers,” HPCA 2007.
  Ebrahimi et al., “Coordinated Control of Multiple Prefetchers in Multi-Core Systems,” MICRO 2009.
  Ebrahimi et al., “Techniques for Bandwidth-Efficient Prefetching of Linked Data Structures in Hybrid Prefetching Systems,” HPCA 2009.
  Ebrahimi et al., “Prefetch-Aware Shared Resource Management for Multi-Core Systems,” ISCA 2011.
  Lee et al., “Prefetch-Aware DRAM Controllers,” MICRO 2008.
Recommended
  Lee et al., “Improving Memory Bank-Level Parallelism in the Presence of Prefetching,” MICRO 2009.

## Slide 8: Videos for Prefetching
Prefetching
  http://www.youtube.com/watch?v=IIkIwiNNl0c&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=29
  http://www.youtube.com/watch?v=yapQavK6LUk&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=30

## Slide 9: Readings for GPUs and SIMD
GPUs and SIMD processing
  Narasiman et al., “Improving GPU Performance via Large Warps and Two-Level Warp Scheduling,” MICRO 2011.
  Jog et al., “OWL: Cooperative Thread Array Aware Scheduling Techniques for Improving GPGPU Performance,” ASPLOS 2013.
  Jog et al., “Orchestrated Scheduling and Prefetching for GPGPUs,” ISCA 2013.
  Lindholm et al., “NVIDIA Tesla: A Unified Graphics and Computing Architecture,” IEEE Micro 2008.
  Fung et al., “Dynamic Warp Formation and Scheduling for Efficient GPU Control Flow,” MICRO 2007.

## Slide 10: Videos for GPUs and SIMD
GPUs and SIMD processing
  Vector/array processing basics: http://www.youtube.com/watch?v=f-XL4BNRoBA&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=15
  GPUs versus other execution models: http://www.youtube.com/watch?v=dl5TZ4-oao0&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=19
  GPUs in more detail: http://www.youtube.com/watch?v=vr5hbSkb1Eg&list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ&index=20

## Slide 11: Online Lectures and More Information
Online Computer Architecture Lectures
  http://www.youtube.com/playlist?list=PL5PHm2jkkXmidJOd59REog9jDnPDTG6IJ
Online Computer Architecture Courses
  Intro: http://www.ece.cmu.edu/~ece447/s13/doku.php
  Advanced: http://www.ece.cmu.edu/~ece740/f11/doku.php
  Advanced: http://www.ece.cmu.edu/~ece742/doku.php
Recent Research Papers
  http://users.ece.cmu.edu/~omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en

## Slide 12: Interconnect Basics

## Slide 13: Interconnect in a Multi-Core System
Shared
Storage

## Slide 14: Where Is Interconnect Used?
To connect components
Many examples
  Processors and processors
  Processors and memories (banks)
  Processors and caches (banks)
  Caches and caches
  I/O devices
Interconnection network

## Slide 15: Why Is It Important?
Affects the scalability of the system
  How large of a system can you build?
  How easily can you add more processors?
Affects performance and energy efficiency
  How fast can processors, caches, and memory communicate?
  How long are the latencies to memory?
  How much energy is spent on communication?

## Slide 16: Interconnection Network Basics
Topology
  Specifies the way switches are wired
  Affects routing, reliability, throughput, latency, building ease
Routing (algorithm)
  How does a message get from source to destination
  Static or adaptive
Buffering and Flow Control
  What do we store within the network?
    Entire packets, parts of packets, etc?
  How do we throttle during oversubscription?
  Tightly coupled with routing strategy

## Slide 17: Topology
Bus (simplest)
Point-to-point connections (ideal and most costly)
Crossbar (less costly)
Ring
Tree
Omega
Hypercube
Mesh
Torus
Butterfly
…

## Slide 18: Metrics to Evaluate Interconnect Topology
Cost
Latency (in hops, in nanoseconds)
Contention
Many others exist you should think about
  Energy
  Bandwidth
  Overall system performance

## Slide 19: Bus
+ Simple
+ Cost effective for a small number of nodes
+ Easy to implement coherence (snooping and serialization)
- Not scalable to large number of nodes (limited bandwidth, electrical loading  reduced frequency)
- High contention  fast saturation
0
1
2
3
4
5
6
7

## Slide 20: Point-to-Point
Every node connected to every other
+ Lowest contention
+ Potentially lowest latency
+ Ideal, if cost is not an issue
-- Highest cost
O(N) connections/ports
per node
O(N2) links
-- Not scalable
-- How to lay out on chip?
0
1
2
3
4
5
6
7

## Slide 21: Crossbar
Every node connected to every other (non-blocking) except one can be using the connection at any given time
Enables concurrent sends to non-conflicting destinations
Good for small number of nodes
+ Low latency and high throughput
- Expensive
- Not scalable  O(N2) cost
- Difficult to arbitrate as N increases
Used in core-to-cache-bank
networks in
- IBM POWER5
- Sun Niagara I/II
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 22: Another Crossbar Design
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 23: Sun UltraSPARC T2 Core-to-Cache Crossbar
High bandwidth interface between 8 cores and 8 L2 banks & NCU
4-stage pipeline: req, arbitration, selection, transmission
2-deep queue for each src/dest pair to hold data transfer request

## Slide 24: Buffered Crossbar
Output
Arbiter
Output
Arbiter
Output
Arbiter
Output
Arbiter
Flow
Control
Flow
Control
Flow
Control
Flow
Control
NI
NI
NI
NI
Buffered
Crossbar
0
1
2
3
NI
NI
NI
NI
Bufferless
Crossbar
0
1
2
3
+ Simpler arbitration/ scheduling
+ Efficient support for variable-size packets
- Requires N2 buffers

## Slide 25: Can We Get Lower Cost than A Crossbar?
Yet still have low contention?
Idea: Multistage networks

## Slide 26: Multistage Logarithmic Networks
Idea: Indirect networks with multiple layers of switches between terminals/nodes
Cost: O(NlogN), Latency: O(logN)
Many variations (Omega, Butterfly, Benes, Banyan, …)
Omega Network:
conflict

## Slide 27: Multistage Circuit Switched
More restrictions on feasible concurrent Tx-Rx pairs
But more scalable than crossbar in cost, e.g., O(N logN) for Butterfly
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 crossbar

## Slide 28: Multistage Packet Switched
Packets “hop” from router to router, pending availability of the next-required switch and buffer
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 router

## Slide 29: Aside: Circuit vs. Packet Switching
Circuit switching sets up full path
  Establish route then send data
  (no one else can use those links)
  + faster arbitration
  -- setting up and bringing down links takes time
Packet switching routes per packet
  Route each packet individually (possibly via different paths)
  if link is free, any packet can use it
  -- potentially slower --- must dynamically switch
  + no setup, bring down time
  + more flexible, does not underutilize links

## Slide 30: Switching vs. Topology
Circuit/packet switching choice independent of topology
It is a higher-level protocol on how a message gets sent to a destination
However, some topologies are more amenable to circuit vs. packet switching

## Slide 31: Another Example: Delta Network
Single path from source to destination
Does not support all possible permutations
Proposed to replace costly crossbars as processor-memory interconnect
Janak H. Patel ,“Processor-Memory Interconnections for Multiprocessors,” ISCA 1979.
8x8 Delta network

## Slide 32: Another Example: Omega Network
Single path from source to destination
All stages are the same
Used in NYU Ultracomputer
Gottlieb et al. “The NYU Ultracomputer-designing a MIMD, shared-memory parallel machine,” ISCA 1982.

## Slide 33: Ring
+ Cheap: O(N) cost
- High latency: O(N)
- Not easy to scale
- Bisection bandwidth remains constant
Used in Intel Haswell, Intel Larrabee, IBM Cell, many commercial systems today
Notes: KSR machine, Hector

## Slide 34: Unidirectional Ring
Simple topology and implementation
  Reasonable performance if N and performance needs (bandwidth & latency) still moderately low
  O(N) cost
  N/2 average hops; latency depends on utilization
R
0
R
1
R
N-2
R
N-1
2
2x2 router

## Slide 35: Bidirectional Rings
+ Reduces latency
+ Improves scalability
- Slightly more complex injection policy (need to select which ring to inject a packet into)

## Slide 36: Hierarchical Rings
+ More scalable
+ Lower latency
- More complex

## Slide 37: More on Hierarchical Rings
Chris Fallin, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, Greg Nazario, Reetuparna Das, and Onur Mutlu, "HiRD: A Low-Complexity, Energy-Efficient Hierarchical Ring Interconnect" SAFARI Technical Report, TR-SAFARI-2012-004, Carnegie Mellon University, December 2012.
Discusses the design and implementation of a mostly-bufferless hierarchical ring

## Slide 38: Mesh
O(N) cost
Average latency: O(sqrt(N))
Easy to layout on-chip: regular and equal-length links
Path diversity: many ways to get from one node to another
Used in Tilera 100-core
And many on-chip network
prototypes
Notes: e.g. Tile64

## Slide 39: Torus
Mesh is not symmetric on edges: performance very sensitive to placement of task on edge vs. middle
Torus avoids this problem
+ Higher path diversity (and bisection bandwidth) than mesh
- Higher cost
- Harder to lay out on-chip
- Unequal link lengths

## Slide 40: Torus, continued
Weave nodes to make inter-node latencies ~constant

## Slide 41: Trees
Planar, hierarchical topology
Latency: O(logN)
Good for local traffic
+ Cheap: O(N) cost
+ Easy to Layout
- Root can become a bottleneck
Fat trees avoid this problem (CM-5)
Fat Tree

## Slide 42: CM-5 Fat Tree
Fat tree based on 4x2 switches
Randomized routing on the way up
Combining, multicast, reduction operators supported in hardware
  Thinking Machines Corp., “The Connection Machine CM-5 Technical Summary,” Jan. 1992.

## Slide 43: Hypercube
Latency: O(logN)
Radix: O(logN)
#links: O(NlogN)
+ Low latency
- Hard to lay out in 2D/3D
0000
0101
0100
0001
0011
0010
0110
0111
1000
1101
1100
1001
1011
1010
1110
1111
Notes: Popular in early message-passing computers (e.g., intel iPSC, NCUBE)

## Slide 44: Caltech Cosmic Cube
64-node message passing machine
Seitz, “The Cosmic Cube,” CACM 1985.

## Slide 45: Handling Contention
Two packets trying to use the same link at the same time
What do you do?
  Buffer one
  Drop one
  Misroute one (deflection)
Tradeoffs?

## Slide 46: Bufferless Deflection Routing
Destination
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.1
1Baran, “On Distributed Communication Networks.” RAND Tech. Report., 1962 / IEEE Trans.Comm., 1964.
New traffic can be injected
whenever there is a free
output link.

## Slide 47: Bufferless Deflection Routing
Input buffers are eliminated: flits are buffered in pipeline latches and on network links
North
South
East
West
Local
North
South
East
West
Local
Deflection Routing Logic
Input Buffers

## Slide 48: Routing Algorithm
Types
  Deterministic: always chooses the same path for a communicating source-destination pair
  Oblivious: chooses different paths, without considering network state
  Adaptive: can choose different paths, adapting to the state of the network
How to adapt
  Local/global feedback
  Minimal or non-minimal paths

## Slide 49: Deterministic Routing
All packets between the same (source, dest) pair take the same path
Dimension-order routing
  E.g., XY routing (used in Cray T3D, and many on-chip networks)
  First traverse dimension X, then traverse dimension Y
+ Simple
+ Deadlock freedom (no cycles in resource allocation)
- Could lead to high contention
- Does not exploit path diversity

## Slide 50: Deadlock
No forward progress
Caused by circular dependencies on resources
Each packet waits for a buffer occupied by another packet downstream

## Slide 51: Handling Deadlock
Avoid cycles in routing
  Dimension order routing
    Cannot build a circular dependency
  Restrict the “turns” each packet can take
Avoid deadlock by adding more buffering (escape paths)
Detect and break deadlock
  Preemption of buffers

## Slide 52: Turn Model to Avoid Deadlock
Idea
  Analyze directions in which packets can turn in the network
  Determine the cycles that such turns can form
  Prohibit just enough turns to break possible cycles
Glass and Ni, “The Turn Model for Adaptive Routing,” ISCA 1992.

## Slide 53: Oblivious Routing: Valiant’s Algorithm
An example of oblivious algorithm
Goal: Balance network load
Idea: Randomly choose an intermediate destination, route to it first, then route from there to destination
  Between source-intermediate and intermediate-dest, can use dimension order routing
+ Randomizes/balances network load
- Non minimal (packet latency can increase)
Optimizations:
  Do this on high load
  Restrict the intermediate node to be close (in the same quadrant)

## Slide 54: Adaptive Routing
Minimal adaptive
  Router uses network state (e.g., downstream buffer occupancy) to pick which “productive” output port to send a packet to
  Productive output port: port that gets the packet closer to its destination
  + Aware of local congestion
  - Minimality restricts achievable link utilization (load balance)
Non-minimal (fully) adaptive
  “Misroute” packets to non-productive output ports based on network state
  + Can achieve better network utilization and load balance
  - Need to guarantee livelock freedom

## Slide 55: On-Chip Networks
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc
  Buses and crossbars are not scalable
Packet switched
2D mesh: Most commonly used topology
Primarily serve cache misses and memory requests
Notes: One commonly proposed solution is on-chip network (NoC), which allows cores to communicate with a packet switched substrate.
Here is a figure showing an on-chip network that uses a 2d-mesh topology which
is commonly used due to its low layout complexity.
This is also the topology we used for our evaluations, but our mechanism is also applicable to other topologies.
In most multi-core systems, NoC primarily serves cache misses and memory requests.

## Slide 56: On-chip Networks
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Router
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)

## Slide 57: On-Chip vs. Off-Chip Interconnects
On-chip advantages
  Low latency between cores
  No pin constraints
  Rich wiring resources
  Very high bandwidth
  Simpler coordination
On-chip constraints/disadvantages
  2D substrate limits implementable topologies
  Energy/power consumption a key concern
  Complex algorithms undesirable
  Logic area constrains use of wiring resources

## Slide 58: On-Chip vs. Off-Chip Interconnects (II)
Cost
  Off-chip: Channels, pins, connectors, cables
  On-chip: Cost is storage and switches (wires are plentiful)
  Leads to networks with many wide channels, few buffers
Channel characteristics
  On chip short distance  low latency
  On chip RC lines  need repeaters every 1-2mm
    Can put logic in repeaters
Workloads
  Multi-core cache traffic vs. supercomputer interconnect traffic

## Slide 59: Motivation for Efficient Interconnect
In many-core chips, on-chip interconnect (NoC) consumes significant power
  Intel Terascale: ~28% of chip power
  Intel SCC: ~10%
  MIT RAW: ~36%
Recent work1 uses bufferless deflection routing to reduce power and die area
Core
L1
L2 Slice
Router
1Moscibroda and Mutlu, “A Case for Bufferless Deflection Routing in On-Chip Networks.” ISCA 2009.

## Slide 60: Research in Interconnects

## Slide 61: Research Topics in Interconnects
Plenty of topics in interconnection networks. Examples:
Energy/power efficient and proportional design
Reducing Complexity: Simplified router and protocol designs
Adaptivity: Ability to adapt to different access patterns
QoS and performance isolation
  Reducing and controlling interference, admission control
Co-design of NoCs with other shared resources
  End-to-end performance, QoS, power/energy optimization
Scalable topologies to many cores, heterogeneous systems
Fault tolerance
Request prioritization, priority inversion, coherence, …
New technologies (optical, 3D)

## Slide 62: One Example: Packet Scheduling
Which packet to choose for a given output port?
  Router needs to prioritize between competing flits
  Which input port?
  Which virtual channel?
  Which application’s packet?
Common strategies
  Round robin across virtual channels
  Oldest packet first (or an approximation)
  Prioritize some virtual channels over others
Better policies in a multi-core environment
  Use application characteristics
  Minimize energy

## Slide 63: Bufferless Routing
  Thomas Moscibroda and Onur Mutlu, "A Case for Bufferless Routing in On-Chip Networks" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 196-207, Austin, TX, June 2009. Slides (pptx)

## Slide 64: On-Chip Networks (NoC)
Connect cores, caches, memory controllers, etc…
Examples:
  Intel 80-core Terascale chip
  MIT RAW chip
Design goals in NoC design:
  High throughput, low latency
  Fairness between cores, QoS, …
  Low complexity, low cost
  Power, low energy consumption
Energy/Power in On-Chip Networks
Power is a key constraint in the design
of high-performance processors
NoCs consume substantial portion of system
power
  ~30% in Intel 80-core Terascale [IEEE Micro’07]
  ~40% in MIT RAW Chip [ISCA’04]
NoCs estimated to consume 100s of Watts [Borkar, DAC’07]

## Slide 65: Current NoC Approaches
Existing approaches differ in numerous ways:
  Network topology [Kim et al, ISCA’07, Kim et al, ISCA’08 etc]
  Flow control [Michelogiannakis et al, HPCA’09, Kumar et al, MICRO’08, etc]
  Virtual Channels [Nicopoulos et al, MICRO’06, etc]
  QoS & fairness mechanisms [Lee et al, ISCA’08, etc]
  Routing algorithms [Singh et al, CAL’04]
  Router architecture [Park et al, ISCA’08]
  Broadcast, Multicast [Jerger et al, ISCA’08, Rodrigo et al, MICRO’08]
Existing work assumes existence of
buffers in routers!

## Slide 66: A Typical Router
Routing Computation
VC Arbiter
Switch Arbiter
VC1
VC2
VCv
VC1
VC2
VCv
Input Port N
Input Port 1
N x N Crossbar
Input Channel 1
Input Channel N
Scheduler
Output Channel 1
Output Channel N
Credit Flow to upstream router
Buffers are integral part of existing NoC Routers
Credit Flow to upstream router

## Slide 67: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Injection Rate
Avg. packet latency
large buffers
medium buffers
small buffers

## Slide 68: Buffers in NoC Routers
Buffers are necessary for high network throughput
 buffers increase total available bandwidth in network
Buffers consume significant energy/power
  Dynamic energy when read/write
  Static energy even when not occupied
Buffers add complexity and latency
  Logic for buffer management
  Virtual channel allocation
  Credit-based flow control
Buffers require significant chip area
  E.g., in TRIPS prototype chip, input buffers occupy 75% of total on-chip network area [Gratz et al, ICCD’06]

## Slide 69: Going Bufferless…?
How much throughput do we lose?
   How is latency affected?
Up to what injection rates can we use bufferless routing?
 Are there realistic scenarios in which NoC is operated at injection rates below the threshold?
Can we achieve energy reduction?
   If so, how much…?
Can we reduce area, complexity, etc…?
Injection Rate
latency
buffers
no buffers

## Slide 70: BLESS: Bufferless Routing
Always forward all incoming flits to some output port
If no productive direction is available, send to another direction
 packet is deflected
 Hot-potato routing [Baran’64, etc]
Buffered
BLESS
Deflected!

## Slide 71: BLESS: Bufferless Routing
Routing
VC Arbiter
Switch Arbiter
Flit-Ranking
Port-Prioritization
arbitration policy
Flit-Ranking
Create a ranking over all incoming flits
Port-Prioritization
For a given flit in this ranking, find the best free output-port
Apply to each flit in order of ranking

## Slide 72: FLIT-BLESS: Flit-Level Routing
Each flit is routed independently.
Oldest-first arbitration (other policies evaluated in paper)
Network Topology:  Can be applied to most topologies (Mesh, Torus, Hypercube, Trees, …) 1) #output ports ¸ #input ports at every router 2) every router is reachable from every other router
Flow Control & Injection Policy:
   Completely local, inject whenever input port is free
Absence of Deadlocks: every flit is always moving
Absence of Livelocks: with oldest-first ranking
Flit-Ranking
Oldest-first ranking
Port-Prioritization
Assign flit to productive port, if possible. Otherwise, assign to non-productive port.

## Slide 73: BLESS with Buffers
BLESS without buffers is extreme end of a continuum
BLESS can be integrated with buffers
  FLIT-BLESS with Buffers
  WORM-BLESS with Buffers
Whenever a buffer is full, it’s first flit becomes must-schedule
must-schedule flits must be deflected if necessary
See paper for details…

## Slide 74: BLESS: Advantages & Disadvantages
Advantages
No buffers
Purely local flow control
Simplicity - no credit-flows - no virtual channels - simplified router design
No deadlocks, livelocks
Adaptivity - packets are deflected around congested areas!
Router latency reduction
Area savings
Disadvantages
Increased latency
Reduced bandwidth
Increased buffering at receiver
Header information at each flit
Oldest-first arbitration complex
QoS becomes difficult
Impact on energy…?

## Slide 75: Reduction of Router Latency
BLESS gets rid of input buffers and virtual channels
BW RC
VA SA
ST
LT
BW
SA
ST
LT
RC
ST
LT
RC
ST
LT
LA LT
BW: Buffer Write
RC: Route Computation
VA: Virtual Channel Allocation
SA: Switch Allocation ST: Switch Traversal
LT: Link Traversal
LA LT: Link Traversal of Lookahead
Baseline Router
(speculative)
head flit
body flit
BLESS Router
(standard)
RC
ST
LT
RC
ST
LT
Router 1
Router 2
Router 1
Router 2
BLESS Router
(optimized)
Router Latency = 3
Router Latency = 2
Router Latency = 1
Can be improved to 2.
[Dally, Towles’04]
our evaluations

## Slide 76: BLESS: Advantages & Disadvantages
Advantages
No buffers
Purely local flow control
Simplicity - no credit-flows - no virtual channels - simplified router design
No deadlocks, livelocks
Adaptivity - packets are deflected around congested areas!
Router latency reduction
Area savings
Disadvantages
Increased latency
Reduced bandwidth
Increased buffering at receiver
Header information at each flit
Impact on energy…?
Extensive evaluations in the paper!

## Slide 77: Evaluation Methodology
2D mesh network, router latency is 2 cycles
  4x4, 8 core, 8 L2 cache banks (each node is a core or an L2 bank)
  4x4, 16 core, 16 L2 cache banks (each node is a core and an L2 bank)
  8x8, 16 core, 64 L2 cache banks (each node is L2 bank and may be a core)
  128-bit wide links, 4-flit data packets, 1-flit address packets
  For baseline configuration: 4 VCs per physical input port, 1 packet deep
Benchmarks
  Multiprogrammed SPEC CPU2006 and Windows Desktop applications
  Heterogeneous and homogenous application mixes
  Synthetic traffic patterns: UR, Transpose, Tornado, Bit Complement
x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  64Kbyte private L1 caches
  Total 16Mbyte shared L2 caches; 16 MSHRs per bank
  DRAM model based on Micron DDR2-800

## Slide 78: Evaluation Methodology
Energy model provided by Orion simulator [MICRO’02]
  70nm technology, 2 GHz routers at 1.0 Vdd
For BLESS, we model
  Additional energy to transmit header information
  Additional buffers needed on the receiver side
  Additional logic to reorder flits of individual packets at receiver
We partition network energy into buffer energy, router energy, and link energy, each having static and dynamic components.
Comparisons against non-adaptive and aggressive adaptive buffered routing algorithms (DO, MIN-AD, ROMM)

## Slide 79: Evaluation – Synthetic Traces
First, the bad news 
Uniform random injection
BLESS has significantly lower saturation throughput compared to buffered baseline.
Chart: Injection Rate (flits per cycle per node)
| 0.0 | 0.08 | 0.16 | 0.07 | 0.08 | 0.09 | 0.1 | 0.11 | 0.12 | 0.13 | 0.14 | 0.15 | 0.16 | 0.17 | 0.18 | 0.19 | 0.2 | 0.21 | 0.22 | 0.23 | 0.24 | 0.25 | 0.26 | 0.27 | 0.28 | 0.29 | 0.3 | 0.31 | 0.32 | 0.33 | 0.34 | 0.35 | 0.36 | 0.37 | 0.38 | 0.39 | 0.4 | 0.41 | 0.42 | 0.43 | 0.44 | 0.45 | 0.46 | 0.47 | 0.48 | 0.49
FLIT-2 | 29.0347 | 29.0347 | 29.0347 | 29.0347 | 29.0347 | 29.3142 | 29.5848 | 29.8829 | 30.2641 | 30.6478 | 31.0371 | 31.5291 | 32.0485 | 32.514 | 33.0424 | 33.6214 | 34.2454 | 34.8647 | 35.5349 | 36.3327 | 37.1874 | 38.0545 | 39.1327 | 40.2686 | 41.8595 | 43.8418 | 48.2112 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
WORM-2 | 29.1135 | 29.1135 | 29.1135 | 29.1135 | 29.1135 | 29.3889 | 29.6607 | 29.9602 | 30.3294 | 30.7091 | 31.1068 | 31.6101 | 32.1665 | 32.6453 | 33.3123 | 33.9411 | 34.7541 | 35.5301 | 36.508 | 37.6649 | 38.9475 | 40.364 | 42.0965 | 44.2469 | 47.7519 | 57.8451 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
FLIT-1 | 22.2481 | 22.2481 | 22.2481 | 22.2481 | 22.2481 | 22.4505 | 22.6682 | 22.8838 | 23.1614 | 23.4459 | 23.7382 | 24.1268 | 24.5155 | 24.8599 | 25.261 | 25.6915 | 26.1454 | 26.6054 | 27.1534 | 27.7909 | 28.4923 | 29.2033 | 30.0413 | 31.1505 | 32.5742 | 34.4702 | 39.8047 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
WORM-1 | 22.3647 | 22.3647 | 22.3647 | 22.3647 | 22.3647 | 22.585 | 22.8079 | 23.0303 | 23.3201 | 23.6314 | 23.9379 | 24.3375 | 24.7663 | 25.1396 | 25.6411 | 26.1686 | 26.7838 | 27.4439 | 28.2236 | 29.1584 | 30.2441 | 31.4552 | 32.9357 | 35.035 | 38.7007 | 61.9914 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101 | 101
MIN-AD | 28.3699 | 28.3699 | 28.3699 | 28.3699 | 28.3699 | 28.5388 | 28.6459 | 28.864 | 29.0263 | 29.2029 | 29.4106 | 29.6055 | 29.7855 | 30.0568 | 30.2965 | 30.5566 | 30.8537 | 31.067 | 31.3404 | 31.6329 | 31.9691 | 32.281 | 32.5873 | 33.0224 | 33.3879 | 33.7872 | 34.2208 | 34.6467 | 35.2042 | 35.8494 | 36.3318 | 36.9534 | 37.7887 | 38.4606 | 39.5018 | 40.4692 | 41.6397 | 43.0612 | 44.6159 | 46.6269 | 49.5462 | 54.2782 | 61.2888 | 82.5748 | 101 | 101
BLESS
Best Baseline

## Slide 80: Evaluation – Homogenous Case Study
milc benchmarks
(moderately intensive)
Perfect caches!
Very little performance degradation with BLESS
(less than 4% in dense network)
With router latency 1, BLESS can even outperform baseline (by ~10%)
Significant energy improvements (almost 40%)
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.991 | 7.9907 | 7.9892 | 7.9789 | 7.9802 | 7.9918 | 7.9907 | 15.6268 | 15.7797 | 15.6253 | 15.2216 | 15.0442 | 15.3638 | 15.2073 | 14.8309 | 14.7752 | 14.7082 | 14.7206 | 14.6774 | 16.2317 | 16.1992
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.40464 | 0.40495 | 0.40517 | 0.42894 | 0.4223 | 0.42804 | 0.42107 | 0.38681 | 0.38681 | 0.391 | 0.43437 | 0.44217 | 0.43081 | 0.43834 | 0.40835 | 0.41014 | 0.41114 | 0.43191 | 0.42337 | 0.37773 | 0.37158
LinkEnergy | 0.12364 | 0.12368 | 0.1237 | 0.14 | 0.14077 | 0.14024 | 0.14058 | 0.1871 | 0.1871 | 0.1874 | 0.23441 | 0.24339 | 0.23441 | 0.24365 | 0.1164 | 0.11652 | 0.11642 | 0.12893 | 0.12753 | 0.12452 | 0.12405
BufferEnergy | 0.47171 | 0.47418 | 0.47432 | 0.045804 | 0.041356 | 0.041234 | 0.043464 | 0.42609 | 0.42609 | 0.42825 | 0.039818 | 0.040263 | 0.039354 | 0.039719 | 0.47526 | 0.48429 | 0.48088 | 0.043196 | 0.038642 | 0.032973 | 0.031075
Baseline
BLESS
RL=1

## Slide 81: Evaluation – Homogenous Case Study
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.991 | 7.9907 | 7.9892 | 7.9789 | 7.9802 | 7.9918 | 7.9907 | 15.6268 | 15.7797 | 15.6253 | 15.2216 | 15.0442 | 15.3638 | 15.2073 | 14.8309 | 14.7752 | 14.7082 | 14.7206 | 14.6774 | 16.2317 | 16.1992
Chart: Energy (normalized)
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
RouterEnergy | 0.40464 | 0.40495 | 0.40517 | 0.42894 | 0.4223 | 0.42804 | 0.42107 | 0.38681 | 0.38681 | 0.391 | 0.43437 | 0.44217 | 0.43081 | 0.43834 | 0.40835 | 0.41014 | 0.41114 | 0.43191 | 0.42337 | 0.37773 | 0.37158
LinkEnergy | 0.12364 | 0.12368 | 0.1237 | 0.14 | 0.14077 | 0.14024 | 0.14058 | 0.1871 | 0.1871 | 0.1874 | 0.23441 | 0.24339 | 0.23441 | 0.24365 | 0.1164 | 0.11652 | 0.11642 | 0.12893 | 0.12753 | 0.12452 | 0.12405
BufferEnergy | 0.47171 | 0.47418 | 0.47432 | 0.045804 | 0.041356 | 0.041234 | 0.043464 | 0.42609 | 0.42609 | 0.42825 | 0.039818 | 0.040263 | 0.039354 | 0.039719 | 0.47526 | 0.48429 | 0.48088 | 0.043196 | 0.038642 | 0.032973 | 0.031075
Baseline
BLESS
RL=1
milc benchmarks
(moderately intensive)
Perfect caches!
Very little performance degradation with BLESS
(less than 4% in dense network)
With router latency 1, BLESS can even outperform baseline (by ~10%)
Significant energy improvements (almost 40%)
Observations:
Injection rates not extremely high on average  self-throttling!
For bursts and temporary hotspots, use network links as buffers!

## Slide 82: Evaluation – Further Results
BLESS increases buffer requirement at receiver by at most 2x  overall, energy is still reduced
Impact of memory latency
 with real caches, very little slowdown! (at most 1.5%)
See paper for details…
Chart: W-Speedup
| DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1 | DO | MIN-AD | ROMM | FLIT-2 | WORM-2 | FLIT-1 | WORM-1
WeightedSpeedup | 7.7417 | 7.7492 | 7.7292 | 7.7059 | 7.7181 | 8.0128 | 7.9959 | 15.0683 | 15.1571 | 15.0648 | 14.9256 | 14.9115 | 15.4871 | 15.381 | 15.2257 | 15.2105 | 15.1846 | 15.2005 | 15.1758 | 16.1669 | 16.1562

## Slide 83: Evaluation – Further Results
BLESS increases buffer requirement at receiver by at most 2x  overall, energy is still reduced
Impact of memory latency
 with real caches, very little slowdown! (at most 1.5%)
Heterogeneous application mixes
(we evaluate several mixes of intensive and non-intensive applications)
 little performance degradation
 significant energy savings in all cases
 no significant increase in unfairness across different applications
Area savings: ~60% of network area can be saved!
See paper for details…

## Slide 84: Evaluation – Aggregate Results
Aggregate results over all 29 applications
Sparse Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -39.4% | -28.1% | -46.4% | -41.0%
∆ System Performance | -0.5% | -3.2% | -0.15% | -0.55%
Chart: Energy (normalized)
| Mean | Worst-Case
RouterEnergy | 0.41542 | 0.44748 | 0.44 | 0.38395 | 0.43429 | 0.44348
LinkEnergy | 0.076955 | 0.094334 | 0.097193 | 0.1754 | 0.22557 | 0.23775
BufferEnergy | 0.50763 | 0.073091 | 0.062562 | 0.44066 | 0.058704 | 0.055516
FLIT
WORM
BASE
FLIT
WORM
BASE
Chart: W-Speedup
| Mean | Worst-Case
WeightedSpeedup | 7.9295 | 7.8761 | 7.8588 | 7.8079 | 7.5574 | 7.4834
FLIT
WORM
BASE

## Slide 85: Evaluation – Aggregate Results
Aggregate results over all 29 applications
Sparse Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -39.4% | -28.1% | -46.4% | -41.0%
∆ System Performance | -0.5% | -3.2% | -0.15% | -0.55%
Dense Network | Perfect L2 |  | Realistic L2 | 
 | Average | Worst-Case | Average | Worst-Case
∆ Network Energy | -32.8% | -14.0% | -42.5% | -33.7%
∆ System Performance | -3.6% | -17.1% | -0.7% | -1.5%

## Slide 86: BLESS Conclusions
For a very wide range of applications and network settings, buffers are not needed in NoC
  Significant energy savings (32% even in dense networks and perfect caches)
  Area-savings of 60%
  Simplified router and network design (flow control, etc…)
  Performance slowdown is minimal (can even increase!)
A strong case for a rethinking of NoC design!
Future research:
  Support for quality of service, different traffic classes, energy-management, etc…

## Slide 87: CHIPPER: A Low-complexity Bufferless Deflection Router
Chris Fallin, Chris Craik, and Onur Mutlu, "CHIPPER: A Low-Complexity Bufferless Deflection Router" Proceedings of the 17th International Symposium on High-Performance Computer Architecture (HPCA), pages 144-155, San Antonio, TX, February 2011. Slides (pptx)

## Slide 88: Motivation
Recent work has proposed bufferless deflection routing (BLESS [Moscibroda, ISCA 2009])
  Energy savings: ~40% in total NoC energy
  Area reduction: ~40% in total NoC area
  Minimal performance loss: ~4% on average
  Unfortunately: unaddressed complexities in router
     long critical path, large reassembly buffers
Goal: obtain these benefits while simplifying the router
in order to make bufferless NoCs practical.
Notes: Router area: see 7.7 in BLESS paper  60.4% * 75% - 18.75% * 25% = 40.6%

## Slide 89: Problems that Bufferless Routers Must Solve
  1. Must provide livelock freedom
   A packet should not be deflected forever
  2. Must reassemble packets upon arrival
Flit: atomic routing unit
0 1 2 3
Packet: one or multiple flits

## Slide 90: A Bufferless Router: A High-Level View
Local Node
Router
Inject
Deflection
Routing
Logic
Crossbar
Reassembly
Buffers
Eject
Problem 2: Packet Reassembly
Problem 1: Livelock Freedom

## Slide 91: Complexity in Bufferless Deflection Routers
  1. Must provide livelock freedom
    Flits are sorted by age, then assigned in age order to output ports
     43% longer critical path than buffered router
  2. Must reassemble packets upon arrival
    Reassembly buffers must be sized for worst case
     4KB per node
    (8x8, 64-byte cache block)

## Slide 92: Problem 1: Livelock Freedom
Inject
Deflection
Routing
Logic
Crossbar
Reassembly
Buffers
Eject
Problem 1: Livelock Freedom

## Slide 93: Livelock Freedom in Previous Work
What stops a flit from deflecting forever?
All flits are timestamped
Oldest flits are assigned their desired ports
Total order among flits
But what is the cost of this?
Flit age forms total order
Guaranteed
progress!
<
<
<
<
<
New traffic is lowest priority

## Slide 94: Age-Based Priorities are Expensive: Sorting
Router must sort flits by age: long-latency sort network
  Three comparator stages for 4 flits
4
1
2
3

## Slide 95: Age-Based Priorities Are Expensive: Allocation
After sorting, flits assigned to output ports in priority order
Port assignment of younger flits depends on that of older flits
  sequential dependence in the port allocator
East?
GRANT: Flit 1  East
DEFLECT: Flit 2  North
GRANT: Flit 3  South
DEFLECT: Flit 4  West
East?
{N,S,W}
{S,W}
{W}
South?
South?
Age-Ordered Flits
1
2
3
4

## Slide 96: Age-Based Priorities Are Expensive
Overall, deflection routing logic based on Oldest-First has a 43% longer critical path than a buffered router
Question: is there a cheaper way to route while guaranteeing livelock-freedom?
Port Allocator
Priority Sort

## Slide 97: Solution: Golden Packet for Livelock Freedom
What is really necessary for livelock freedom?
Key Insight: No total order. it is enough to:
1. Pick one flit to prioritize until arrival
2. Ensure any flit is eventually picked
Flit age forms total order
Guaranteed
progress!
New traffic is
lowest-priority
<
<
<
Guaranteed
progress!
<
“Golden Flit”
partial ordering is sufficient!

## Slide 98: What Does Golden Flit Routing Require?
Only need to properly route the Golden Flit
First Insight: no need for full sort
Second Insight: no need for sequential allocation
Port Allocator
Priority Sort

## Slide 99: Golden Flit Routing With Two Inputs
Let’s route the Golden Flit in a two-input router first
Step 1: pick a “winning” flit: Golden Flit, else random
Step 2: steer the winning flit to its desired output
and deflect other flit
   Golden Flit always routes toward destination

## Slide 100: Golden Flit Routing with Four Inputs
Each block makes decisions independently!
  Deflection is a distributed decision
N
E
S
W
N
S
E
W

## Slide 101: Permutation Network Operation
N
E
S
W
wins  swap!
wins  no swap!
wins  no swap!
deflected
Golden:
wins  swap!
x
Port Allocator
Priority Sort
N
E
S
W
N
S
E
W

## Slide 102: Problem 2: Packet Reassembly
Inject/Eject
Reassembly
Buffers
Inject
Eject

## Slide 103: Reassembly Buffers are Large
Worst case: every node sends a packet to one receiver
Why can’t we make reassembly buffers smaller?
Node 0
Node 1
Node N-1
Receiver
one packet in flight
per node
N sending nodes
…
O(N) space!

## Slide 104: Small Reassembly Buffers Cause Deadlock
What happens when reassembly buffer is too small?
Network
cannot eject:
reassembly
buffer full
reassembly
buffer
Many Senders
One Receiver
Remaining flits
must inject for
forward progress
cannot inject new traffic
network full

## Slide 105: Reserve Space to Avoid Deadlock?
What if every sender asks permission from the receiver before it sends?
 adds additional delay to every request
reassembly buffers
Reserve Slot?
Reserved
ACK
Sender
Reserve Slot
ACK
Send Packet
Receiver

## Slide 106: Escaping Deadlock with Retransmissions
Sender is optimistic instead: assume buffer is free
  If not, receiver drops and NACKs; sender retransmits
   no additional delay in best case
   transmit buffering overhead for all packets
   potentially many retransmits
Reassembly
Buffers
Retransmit
Buffers
NACK!
Sender
ACK
Receiver
Send (2 flits)
Drop, NACK
Other packet completes
Retransmit packet
ACK
Sender frees data

## Slide 107: Solution: Retransmitting Only Once
Key Idea: Retransmit only when space becomes available.
   Receiver drops packet if full; notes which packet it drops
   When space frees up, receiver reserves space so
  retransmit is successful
   Receiver notifies sender to retransmit
Reassembly
Buffers
Retransmit
Buffers
NACK
Sender
Reserved
Receiver
Pending: Node 0 Req 0

## Slide 108: Using MSHRs as Reassembly Buffers
Inject/Eject
Reassembly
Buffers
Inject
Eject
Miss Buffers (MSHRs)
C Using miss buffers for reassembly makes this a
truly bufferless network.

## Slide 109: CHIPPER: Cheap Interconnect Partially-Permuting Router
Inject
Deflection
Routing
Logic
Crossbar
Reassembly
Buffers
Eject
Baseline Bufferless Deflection Router
Large buffers for worst case
Retransmit-Once
Cache buffers
Long critical path:
1. Sort by age
2. Allocate ports sequentially
Golden Packet
 Permutation Network

## Slide 110: CHIPPER: Cheap Interconnect Partially-Permuting Router
Inject/Eject
Miss Buffers (MSHRs)
Inject
Eject

## Slide 111: EVALUATION

## Slide 112: Methodology
Multiprogrammed workloads: CPU2006, server, desktop
  8x8 (64 cores), 39 homogeneous and 10 mixed sets
Multithreaded workloads: SPLASH-2, 16 threads
  4x4 (16 cores), 5 applications
System configuration
  Buffered baseline: 2-cycle router, 4 VCs/channel, 8 flits/VC
  Bufferless baseline: 2-cycle latency, FLIT-BLESS
  Instruction-trace driven, closed-loop, 128-entry OoO window
  64KB L1, perfect L2 (stresses interconnect), XOR mapping

## Slide 113: Methodology
Hardware modeling
  Verilog models for CHIPPER, BLESS, buffered logic
    Synthesized with commercial 65nm library
  ORION for crossbar, buffers and links
Power
  Static and dynamic power from hardware models
  Based on event counts in cycle-accurate simulations

## Slide 114: Results: Performance Degradation
Chart: Multithreaded
| luc | cholesky | radix | fft | lun | AVG
Buffered | 1 | 1 | 1 | 1 | 1 | 1
BLESS | 1.0029 | 1.0018 | 0.98947 | 0.98772 | 1.0053 | 0.99744
CHIPPER | 1.0018 | 1.0012 | 0.97236 | 0.96885 | 0.96259 | 0.98136
Chart: Multiprogrammed (subset of 49 total)
| perlbench | tonto | gcc | h264ref | vpr | search.1 | MIX.5 | MIX.2 | MIX.8 | MIX.0 | MIX.6 | GemsFDTD | stream | mcf | AVG (full set)
Buffered | 63.9797 | 63.6791 | 63.5732 | 63.3609 | 61.1795 | 60.5003 | 60.4737 | 60.2887 | 57.7855 | 57.6859 | 57.4864 | 48.0577 | 41.9916 | 22.5714 | 55.5307
BLESS | 63.9892 | 63.8161 | 63.7649 | 63.649 | 61.6634 | 60.0978 | 60.0345 | 60.1977 | 56.4544 | 56.4568 | 56.6327 | 43.5859 | 31.6 | 15.4656 | 53.4814
CHIPPER | 63.9875 | 63.7929 | 63.7101 | 63.5642 | 57.5277 | 54.6854 | 56.5988 | 57.3718 | 50.003 | 51.7054 | 51.2283 | 33.0817 | 22.1335 | 11.3238 | 49.5151
13.6%
1.8%
3.6%
49.8%
C Minimal loss for low-to-medium-intensity workloads

## Slide 115: Results: Power Reduction
Chart: Multiprogrammed (subset of 49 total)
| perlbench | tonto | gcc | h264ref | vpr | search.1 | MIX.5 | MIX.2 | MIX.8 | MIX.0 | MIX.6 | GemsFDTD | stream | mcf | AVG (full set)
Buffered | 5.8772 | 6.2615 | 6.3198 | 6.475 | 9.5689 | 10.1378 | 10.0346 | 9.6586 | 10.9838 | 11.0939 | 11.07 | 12.8089 | 14.8531 | 15.3401 | 9.8883
BLESS | 1.1599 | 1.444 | 1.4834 | 1.6039 | 4.2738 | 5.3655 | 5.2363 | 4.8336 | 6.7843 | 6.7853 | 6.6748 | 9.04 | 10.3725 | 10.7364 | 5.275
CHIPPER | 0.94114 | 1.2232 | 1.2651 | 1.3849 | 4.1573 | 5.3494 | 4.622 | 4.3107 | 6.1701 | 6.2371 | 6.0794 | 8.0081 | 9.9745 | 10.209 | 4.924
Chart: Multithreaded
| luc | cholesky | radix | fft | lun | AVG
Buffered | 1.5231 | 1.4974 | 1.652 | 1.6945 | 2.0545 | 1.6843
BLESS | 0.33073 | 0.31291 | 0.51824 | 0.55499 | 0.81791 | 0.50696
CHIPPER | 0.27643 | 0.25857 | 0.47897 | 0.52078 | 0.77466 | 0.46188
54.9%
73.4%
C Removing buffers  majority of power savings
C Slight savings from BLESS to CHIPPER

## Slide 116: Results: Area and Critical Path Reduction
Chart: Normalized Router Area
| Buffered | BLESS | CHIPPER
Area | 1 | 0.6478 | 0.63761
Chart: Normalized Critical Path
| Buffered | BLESS | CHIPPER
Critical Path | 1 | 1.4255 | 1.0106
-36.2%
-29.1%
+1.1%
-1.6%
C CHIPPER maintains area savings of BLESS
C Critical path becomes competitive to buffered

## Slide 117: Conclusions
Two key issues in bufferless deflection routing
  livelock freedom and packet reassembly
Bufferless deflection routers were high-complexity and impractical
  Oldest-first prioritization  long critical path in router
  No end-to-end flow control for reassembly  prone to deadlock with reasonably-sized reassembly buffers
CHIPPER is a new, practical bufferless deflection router
  Golden packet prioritization  short critical path in router
  Retransmit-once protocol  deadlock-free packet reassembly
  Cache miss buffers as reassembly buffers  truly bufferless network
CHIPPER frequency comparable to buffered routers at much lower area and power cost, and minimal performance loss

## Slide 118: MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect
Chris Fallin, Greg Nazario, Xiangyao Yu, Kevin Chang, Rachata Ausavarungnirun, and Onur Mutlu, "MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect" Proceedings of the 6th ACM/IEEE International Symposium on Networks on Chip (NOCS), Lyngby, Denmark, May 2012. Slides (pptx) (pdf)

## Slide 119: Bufferless Deflection Routing
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.
Removing buffers yields significant benefits
  Reduces power (CHIPPER: reduces NoC power by 55%)
  Reduces die area (CHIPPER: reduces NoC area by 36%)
But, at high network utilization (load), bufferless deflection routing causes unnecessary link & router traversals
  Reduces network throughput and application performance
  Increases dynamic power
Goal: Improve high-load performance of low-cost deflection networks by reducing the deflection rate.

## Slide 120: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 121: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 122: Issues in Bufferless Deflection Routing
Correctness: Deliver all packets without livelock
  CHIPPER1: Golden Packet
  Globally prioritize one packet until delivered
Correctness: Reassemble packets without deadlock
  CHIPPER1: Retransmit-Once
Performance: Avoid performance degradation at high load
  MinBD
1 Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.

## Slide 123: Key Performance Issues
1. Link contention: no buffers to hold traffic  any link contention causes a deflection
 use side buffers
2. Ejection bottleneck: only one flit can eject per router per cycle  simultaneous arrival causes deflection
 eject up to 2 flits/cycle
3. Deflection arbitration: practical (fast) deflection arbiters deflect unnecessarily
 new priority scheme (silver flit)

## Slide 124: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 125: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 126: Addressing Link Contention
Problem 1: Any link contention causes a deflection
Buffering a flit can avoid deflection on contention
But, input buffers are expensive:
  All flits are buffered on every hop  high dynamic energy
  Large buffers necessary  high static energy and large area
Key Idea 1: add a small buffer to a bufferless deflection router to buffer only flits that would have been deflected

## Slide 127: How to Buffer Deflected Flits
Baseline Router
Eject
Inject
1 Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.
Destination
Destination
DEFLECTED

## Slide 128: How to Buffer Deflected Flits
Side-Buffered Router
Eject
Inject
Step 1. Remove up to one deflected flit per cycle from the outputs.
Step 2. Buffer this flit in a small FIFO “side buffer.”
Step 3. Re-inject this flit into pipeline when a slot is available.
Side Buffer
Destination
Destination
DEFLECTED

## Slide 129: Why Could A Side Buffer Work Well?
Buffer some flits and deflect other flits at per-flit level
  Relative to bufferless routers, deflection rate reduces (need not deflect all contending flits)
   4-flit buffer reduces deflection rate by 39%
  Relative to buffered routers, buffer is more efficiently used (need not buffer all flits)
     similar performance with 25% of buffer space

## Slide 130: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 131: Addressing the Ejection Bottleneck
Problem 2: Flits deflect unnecessarily because only one flit can eject per router per cycle
In 20% of all ejections, ≥ 2 flits could have ejected  all but one flit must deflect and try again
 these deflected flits cause additional contention
Ejection width of 2 flits/cycle reduces deflection rate 21%
Key idea 2: Reduce deflections due to a single-flit ejection port by allowing two flits to eject per cycle

## Slide 132: Addressing the Ejection Bottleneck
Single-Width Ejection
Eject
Inject
DEFLECTED

## Slide 133: Addressing the Ejection Bottleneck
Dual-Width Ejection
Eject
Inject
For fair comparison, baseline routers have dual-width ejection for perf. (not power/area)

## Slide 134: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 135: Improving Deflection Arbitration
Problem 3: Deflections occur unnecessarily because fast arbiters must use simple priority schemes
Age-based priorities (several past works): full priority order gives fewer deflections, but requires slow arbiters
State-of-the-art deflection arbitration (Golden Packet & two-stage permutation network)
  Prioritize one packet globally (ensure forward progress)
  Arbitrate other flits randomly (fast critical path)
Random common case leads to uncoordinated arbitration

## Slide 136: Fast Deflection Routing Implementation
Let’s route in a two-input router first:
Step 1: pick a “winning” flit (Golden Packet, else random)
Step 2: steer the winning flit to its desired output
and deflect other flit
   Highest-priority flit always routes to destination

## Slide 137: Fast Deflection Routing with Four Inputs
Each block makes decisions independently
  Deflection is a distributed decision
N
E
S
W
N
S
E
W

## Slide 138: Unnecessary Deflections in Fast Arbiters
How does lack of coordination cause unnecessary deflections?
  1. No flit is golden (pseudorandom arbitration)
  2. Red flit wins at first stage
  3. Green flit loses at first stage (must be deflected now)
  4. Red flit loses at second stage; Red and Green are deflected
Destination
Destination
all flits have
equal priority
unnecessary
deflection!

## Slide 139: Improving Deflection Arbitration
Key idea 3: Add a priority level and prioritize one flit to ensure at least one flit is not deflected in each cycle
Highest priority: one Golden Packet in network
  Chosen in static round-robin schedule
  Ensures correctness
Next-highest priority: one silver flit per router per cycle
  Chosen pseudo-randomly & local to one router
  Enhances performance

## Slide 140: Adding A Silver Flit
Randomly picking a silver flit ensures one flit is not deflected
  1. No flit is golden but Red flit is silver
  2. Red flit wins at first stage (silver)
  3. Green flit is deflected at first stage
  4. Red flit wins at second stage (silver); not deflected
Destination
Destination
At least one flit
is not deflected
red flit has
higher priority
all flits have
equal priority

## Slide 141: Minimally-Buffered Deflection Router
Eject
Inject
Problem 1: Link Contention
Solution 1: Side Buffer
Problem 2: Ejection Bottleneck
Solution 2: Dual-Width Ejection
Problem 3: Unnecessary Deflections
Solution 3: Two-level priority scheme

## Slide 142: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration

## Slide 143: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 144: Methodology: Simulated System
Chip Multiprocessor Simulation
  64-core and 16-core models
  Closed-loop core/cache/NoC cycle-level model
  Directory cache coherence protocol (SGI Origin-based)
  64KB L1, perfect L2 (stresses interconnect), XOR-mapping
  Performance metric: Weighted Speedup (similar conclusions from network-level latency)
  Workloads: multiprogrammed SPEC CPU2006
    75 randomly-chosen workloads
    Binned into network-load categories by average injection rate

## Slide 145: Methodology: Routers and Network
Input-buffered virtual-channel router
  8 VCs, 8 flits/VC [Buffered(8,8)]: large buffered router
  4 VCs, 4 flits/VC [Buffered(4,4)]: typical buffered router
  4 VCs, 1 flit/VC [Buffered(4,1)]: smallest deadlock-free router
  All power-of-2 buffer sizes up to (8, 8) for perf/power sweep
Bufferless deflection router: CHIPPER1
Bufferless-buffered hybrid router: AFC2
  Has input buffers and deflection routing logic
  Performs coarse-grained (multi-cycle) mode switching
Common parameters
  2-cycle router latency, 1-cycle link latency
  2D-mesh topology (16-node: 4x4; 64-node: 8x8)
  Dual ejection assumed for baseline routers (for perf. only)
1Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.
2Jafri et al., “Adaptive Flow Control for Robust Performance and Energy”, MICRO 2010.

## Slide 146: Methodology: Power, Die Area, Crit. Path
Hardware modeling
  Verilog models for CHIPPER, MinBD, buffered control logic
    Synthesized with commercial 65nm library
  ORION 2.0 for datapath: crossbar, muxes, buffers and links
Power
  Static and dynamic power from hardware models
  Based on event counts in cycle-accurate simulations
  Broken down into buffer, link, other

## Slide 147: Reduced Deflections & Improved Perf.
Deflection
Chart: Weighted Speedup
| AVG
Baseline | 13.3104
B (Side-Buf) | 12.7312
D (Dual-Eject) | 13.8075
S (Silver Flits) | 13.402
B+D | 14.0867
B+S+D (MinBD) | 14.1847
Rate
28%
17%
22%
27%
11%
10%
All mechanisms individually reduce deflections
2. Side buffer alone is not sufficient for performance (ejection bottleneck remains)
3. Overall, 5.8% over baseline, 2.7% over dual-eject by reducing deflections 64% / 54%
5.8%
2.7%

## Slide 148: Overall Performance Results
Chart: Injection Rate
| 0.0 - 0.15 | 0.15 - 0.30 | 0.30 - 0.40 | 0.40 - 0.50 | > 0.50 | AVG
Buffered (8,8) | 16.0051 | 15.8617 | 15.1919 | 14.2118 | 11.8768 | 14.6295
Buffered (4,4) | 16.0049 | 15.8602 | 15.1612 | 14.1471 | 11.7073 | 14.5761
Buffered (4,1) | 15.9983 | 15.8027 | 14.8748 | 13.5043 | 10.4798 | 14.132
CHIPPER | 15.9451 | 15.4841 | 14.5144 | 13.1601 | 9.9339 | 13.8075
AFC (4,4) | 15.9907 | 15.8249 | 15.1374 | 14.1132 | 10.872 | 14.3876
MinBD-4 | 15.919 | 15.5898 | 14.893 | 13.7518 | 10.7399 | 14.1787
Improves 2.7% over CHIPPER (8.1% at high load)
Similar perf. to Buffered (4,1) @ 25% of buffering space
2.7%
8.1%
2.7%
8.3%
Within 2.7% of Buffered (4,4) (8.3% at high load)

## Slide 149: Overall Power Results
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
static | 1.6291 | 1.047 | 0.74594 | 0.52767 | 0.86902 | 0.55326
dynamic | 0.92052 | 0.79869 | 0.70841 | 0.92607 | 0.84745 | 0.70553
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
buffer | 1.0994 | 0.40037 | 0.04931 | 0 | 0.24432 | 0.023553
non-buffer | 1.4502 | 1.4453 | 1.405 | 1.4537 | 1.4721 | 1.2352
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
static buffer | 0.91433 | 0.3323 | 0.031218 | 0 | 0.13325 | 0.020768
static link | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115
static other | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099
dynamic buffer | 0.18502 | 0.068074 | 0.018092 | 0 | 0.11107 | 0.0027846
dynamic link | 0.59769 | 0.59372 | 0.56097 | 0.71132 | 0.59769 | 0.53927
dynamic other | 0.13782 | 0.1369 | 0.12935 | 0.21475 | 0.13869 | 0.16348
Buffers are significant fraction of power in baseline routers
Buffer power is much smaller in MinBD (4-flit buffer)
Dynamic power increases with deflection routing
Dynamic power reduces in MinBD relative to CHIPPER

## Slide 150: Performance-Power Spectrum
Chart: Network Power (W)
| 2.549584000000001 | 2.248441 | 2.085126000000001 | 1.522975 | 2.000121000000006 | 1.845714 | 1.753193 | 1.454351 | 1.723579 | 1.637617 | 1.57499 | 1.401160999999997 | 1.578871 | 1.463406 | 1.520311 | 1.344364
 | 14.6295 | 14.612 | 14.5288 | 14.3117 | 14.6259 | 14.5761 | 14.4304 | 14.132 | 14.6045 | 14.4883 | 14.247 | 13.8303 | 14.523 | 13.9062 | 14.304 | 13.3269
 | 14.3876
 | 13.8075
 | 14.1787
Most energy-efficient (perf/watt) of any evaluated network router design
Buf (4,4)
Buf (4,1)
More Perf/Power
Less Perf/Power
Buf (8,8)
AFC
CHIPPER
MinBD

## Slide 151: Die Area and Critical Path
Chart: Normalized Die Area
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | MinBD
Area | 2.06 | 1.69 | 1.6 | 1 | 1.03
Chart: Normalized Critical Path
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | MinBD
Critical Path | 0.99 | 0.99 | 0.99 | 1 | 1.07
Only 3% area increase over CHIPPER (4-flit buffer)
Reduces area by 36% from Buffered (4,4)
Increases by 7% over CHIPPER, 8% over Buffered (4,4)
+3%
-36%
+7%
+8%

## Slide 152: Conclusions
Bufferless deflection routing offers reduced power & area
But, high deflection rate hurts performance at high load
MinBD (Minimally-Buffered Deflection Router) introduces:
  Side buffer to hold only flits that would have been deflected
  Dual-width ejection to address ejection bottleneck
  Two-level prioritization to avoid unnecessary deflections
MinBD yields reduced power (31%) & reduced area (36%) relative to buffered routers
MinBD yields improved performance (8.1% at high load) relative to bufferless routers  closes half of perf. gap
MinBD has the best energy efficiency of all evaluated designs with competitive performance

## Slide 153: More Readings
Studies of congestion and congestion control in on-chip vs. internet-like networks
George Nychis, Chris Fallin, Thomas Moscibroda, Onur Mutlu, and Srinivasan Seshan, "On-Chip Networks from a Networking Perspective: Congestion and Scalability in Many-core Interconnects" Proceedings of the 2012 ACM SIGCOMM Conference (SIGCOMM), Helsinki, Finland, August 2012. Slides (pptx)
George Nychis, Chris Fallin, Thomas Moscibroda, and Onur Mutlu, "Next Generation On-Chip Networks: What Kind of Congestion Control Do We Need?" Proceedings of the 9th ACM Workshop on Hot Topics in Networks (HOTNETS), Monterey, CA, October 2010. Slides (ppt) (key)

## Slide 154: HAT: Heterogeneous Adaptive Throttling for On-Chip Networks
Kevin Chang, Rachata Ausavarungnirun, Chris Fallin, and Onur Mutlu, "HAT: Heterogeneous Adaptive Throttling for On-Chip Networks" Proceedings of the 24th International Symposium on Computer Architecture and High Performance Computing (SBAC-PAD), New York, NY, October 2012. Slides (pptx) (pdf)
Notes: Name: … phd student from CMU
Ttitle
collaborative work done with rachata, chris, and Dr. Onur Mutlu

## Slide 155: Executive Summary
Problem: Packets contend in on-chip networks (NoCs), causing congestion, thus reducing performance
Observations:
1) Some applications are more sensitive to network latency than others 2) Applications must be throttled differently to achieve peak performance
Key Idea: Heterogeneous Adaptive Throttling (HAT) 1) Application-aware source throttling 2) Network-load-aware throttling rate adjustment
Result: Improves performance and energy efficiency over state-of-the-art source throttling policies
Notes: Here is a one slide summary of what I’ll present today
One major problems is that packets … which causes congestion. As a result, this reduces system performance due to increased network latency.
We make two key observations in this work:
First, some apps are more sen to network latency than others
Second, apps ……
Based on these two key observations, we develop a new source throttling mechanism called HAT to mitigate the detrimental effect of congestion.
It has two key components:
First, HAT performs app-aware source throttling, which selectively throttles certain applications.
Second, BLUE, which dynamically adjusts throttling rate to achieve high perf
Our evaluation shows that HAT improves perf…..

## Slide 156: Outline
Background and Motivation
Mechanism
Prior Works
Results
Notes: Here is the outline for the talk.
I’ve briefly talked about some background on nocs.
Next I’ll talk about the motivation and key idea of our work.

## Slide 157: On-Chip Networks
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc
Packet switched
2D mesh: Most commonly used topology
Primarily serve cache misses and memory requests
Router designs
  Buffered: Input buffers to hold contending packets
  Bufferless: Misroute (deflect) contending packets
Notes: In multi-core processors, interconnect serves as a communication substrate for cores, caches, ….
However as core count continues to increase, conventional interconnects such as busses and crossbards no longer scale adequately.
The commonly proposed solution is on-chip network, which allows cores to communicate with a packet switched substrate.
Here is a figure showing an on-chip network that uses a 2d-mesh topology which
Is commonly used due to its low layout complexity.
In most multi-core systems, NoC primarily serves cache misses and memory requests.
A conventional router design for an on-chip network often have input buffers to hold ….
Alternatively, some other router designs have proposed eliminating these buffers and instead deflect contending packets to different links.

## Slide 158: Network Congestion Reduces Performance
Network congestion:
Network throughput
Application performance
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
P
P
P
P
P
Congestion
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
P
Packet
Limited shared resources (buffers and links)
Design constraints: power, chip area, and timing
Notes: In modern multicore systems, NoC has limited shared resources due to various design constraints, such as power, chip area and timing.
Therefore, Noc will sometimes experience network congestion when there is a large amount of traffic.
Network congestion reduces network throughput, and hence application performance.
Here is a quick illustration on showing how congestion can occur in a network. Four different nodes send their packets (the red packets) to a central node.
since there is no free output link at the central node, the yellow packet cannot be injected into the network, which produces congestion.
------------------------------------------------------------------------------------------------
Injection only when output link is free. Put this in the slide?
Network congestion has detrimental an effect on the system performance.
--------------
Content: Higher network load leads to more congestion

## Slide 159: Goal
Improve performance in a highly congested NoC
Reducing network load decreases network congestion, hence improves performance
Approach: source throttling to reduce network load
  Temporarily delay new traffic injection
Naïve mechanism: throttle every single node
Notes: In this work, our goal is to improve application performance in a highly congested noc.
To achieve this, we observe that reducing network load leads to lower network congestion, hence improving performance.
To reduce network load, we take the approach of source throttling, which temporarily delays new traffic injection.
Although packet injections are delayed due to throttling, performance can still be improved b/c of less congestion in the network.
A naïve way of source throttling is to block injection of every node. However, this does not work well.
Now we will go through some key observations on how to design high-performance source throttling mechanism.
Soft throttling: inject with non-zero probability
Throttling rate: 0% (unthrottled) <-> 100% (fully blocked)
Key question:
Which application to throttle?
How aggressive do we throttle them?

## Slide 160: Key Observation #1
Chart: Normalized Performance
| mcf | gromacs | system
Throttle gromacs | 1 | 0.96 | 0.98
Throttle mcf | 1.05 | 1.14 | 1.09
gromacs: network-non-intensive
+ 9%
- 2%
Different applications respond differently to changes in network latency
mcf: network-intensive
Throttling mcf reduces congestion
gromacs is more sensitive to network latency
Throttling network-intensive applications benefits system performance more
Notes: Our first key observation is that different apps…..
To illustrate this point, we set up an experiment with a 16-node system running 8 copies of gromacs, which is a network-non-intensive spec benchmark,
and 8 copies of mcf, which is a network-intensive spec benchmark.
The figure shows the performance of this workload when different app is throttled at a fixed throttling rate.
The blue bar corresponds to throttling only gromcas
and the red bar corresponds to throttling only mcf
The yaxis indicate normalized performance to the baseline without throttling.
The xaxis shows three throughput measurements
The figure shows that when ONLY gromacs is throttled, the average system performance actually decreases by 2%,
On the other hand, when mcf is throttled the average perf increases by 9%.
This is because throttling mcf, which is network instensive, “significantly” reduces network load, and
it allows gromacs to make much faster progress with less latency since it’s more sensitive to latency.
**** Allowing gromacs to send packets with less latency is more beneficial because gromacs injects fewer number of packets and each packet represents a greater forward progress for the application ****
X: Therefore, non-intensive application is more sensitive to increases in network latency.
In the sum, throttling network-intensive applications benefits system performance more than ….
Gromacs:
1) not only do we not reduce congestion, but we also decrease performance by 2%
2)
Delete lines:
gromacs benefits more from reduced network latency
gromacs injects fewer packets, thus each packet represents a greater forward progress

## Slide 161: Key Observation #2
Chart: Throttling Rate (%)
| 80.0 | 82.0 | 84.0 | 86.0 | 88.0 | 90.0 | 92.0 | 94.0 | 96.0 | 98.0 | 100.0
Workload 1 | 9.6783 | 9.6962 | 9.7273 | 9.7829 | 9.8607 | 9.9987 | 10.286 | 10.713 | 9.5421 | 7.5361
Workload 2 | 10.3198 | 10.3497 | 10.3935 | 10.4632 | 10.6088 | 10.8432 | 11.1523 | 10.9859 | 9.6724 | 7.6214
Workload 3 | 14.5502 | 14.5837 | 14.6565 | 14.7872 | 15.0076 | 15.2556 | 15.1927 | 14.4139 | 12.8768 | 10.7685
Different workloads achieve peak performance at different throttling rates
Dynamically adjusting throttling rate yields better performance than a single static rate
90%
92%
94%
Notes: Our second key observation is that ….
To illustrate the benefits of using different throttling rate,
we evaluate system performance of three heterogeneous application workloads on a 16-core system with varying throttling rate.
The yaxis indicates sys perf in terms of WS
X-axis: shows the static throttling rate applied to each workload.
As we can see, different workloads require different throttling rate to achieve peak performance (in the example, 94% for wk1)
As a result, dynamically adjusting throttling rate yields better perf than a single static rate.

## Slide 162: Outline
Background and Motivation
Mechanism
Prior Works
Results
Notes: Next we will talk about our mechanism which is built on top of these key observations.

## Slide 163: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjusts throttling rate to adapt to different workloads
Notes: Putting these observations together, we propose a new source throttling mechanism called Heterogeneous Adaptive Throttling (HAT)
There are two key components:
The first key component is app-aware throttling.
HAT throttles network-intensive apps that interfere with network-non-intensive applications to reduce network congestion
X: and allow non-intensive app to make faster forward progress.
2.The second key component is network-load….
HAT … read bullet, so that it provides high performance

## Slide 164: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjusts throttling rate to adapt to different workloads
Notes: Next I will talk about how HAT achieves app-aware throttling

## Slide 165: Application-Aware Throttling
Measure Network Intensity Use L1 MPKI (misses per thousand instructions) to estimate network intensity
Classify Application
  Sort applications by L1 MPKI
Throttle network-intensive applications
App
Σ MPKI < NonIntensiveCap
Network-non-intensive
Network-intensive
Higher L1 MPKI
Throttle
Notes: To perform app throttling, HAT first measures each application’s network intensity.
Since NoC primarily serves L1 cache misses in our evaluated system, we use L1 MPKI as a proxy to intensity.
  Once applications’ intensity is measured,
  HAT needs to classify applications as network-intensive or network-non intensive.
  To do so, HAT first sorts apps by their measured L1 MPKI. Next starting from the least mpki app,
  the applications are classified as network non intensive until their sum of MPKI exceeds a pre-set threshold,
  which we call it NonIntensiveCap.
  CAP ensures that the traffic of non-intensive applications provides sufficient load without causing severe network congestion.
  So it should be scaled with network capacity and tuned for the particular network design.
  All remaining applications are then considered as network intensive.
  When all applications are classified, HAT applies throttling to network-intensive applications.
  ****** KEY idea again*******
  Again, the reason to throttle them is to reduce congestion and allow non-intensive app,
  which are more sensitive to network latency, to send packets through the network more quickly.
  X: because a singe packet of a net-non-intensive app represents a greater forward progress,
  so throttling intensive app allows non-intensive app to get through the network more quickly.

## Slide 166: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjusts throttling rate to adapt to different workloads
Notes: Now we will talk about the second key component of HAT

## Slide 167: Dynamic Throttling Rate Adjustment
For a given network design, peak performance tends to occur at a fixed network load point
Dynamically adjust throttling rate to achieve that network load point
Notes: We observe that *PT1.
Thus, we dyn****
In our work, we empirically determine the peak network load point.

## Slide 168: Dynamic Throttling Rate Adjustment
Goal: maintain network load at a peak performance point
Measure network load
Compare and adjust throttling rate
  If network load > peak point:
  Increase throttling rate
  elif network load ≤ peak point:
  Decrease throttling rate
Notes: To achieve the goal of maintaining ….
HAT performs the following operations.
First it measures network load
HAT compares the current network load with the peak point and adjust throttling rate accordingly.
Increase th rate to reduce network load
Else…. Rate to allow more traffic to inject into the network

## Slide 169: Epoch-Based Operation
Continuous HAT operation is expensive
Solution: performs HAT at epoch granularity
Time
Current Epoch
(100K cycles)
Next Epoch
(100K cycles)
During epoch:
Measure L1 MPKI of each application
Measure network load
Beginning of epoch:
Classify applications
Adjust throttling rate
Reset measurements
Notes: Since continuously performing HAT’s operations is expensive,
we want to reduce the computation overhead by performing HAT at epoch gran.
Epoch length is 100K cycles
During an epoch….
Once an epoch finishes, hat uses these measurements to classify applications, and adjust throttling rate.
At the end, we reset the monitor counters to start new measurements.

## Slide 170: Outline
Background and Motivation
Mechanism
Prior Works
Results
Notes: To this end, we have presented HAT.
Now let’s take a look at prior works

## Slide 171: Prior Source Throttling Works
Source throttling for bufferless NoCs [Nychis+ Hotnets’10, SIGCOMM’12]
  Application-aware throttling based on starvation rate
  Does not adaptively adjust throttling rate
  “Heterogeneous Throttling”
Source throttling off-chip buffered networks [Thottethodi+ HPCA’01]
  Dynamically trigger throttling based on fraction of buffer occupancy
  Not application-aware: fully block packet injections of every node
  “Self-tuned Throttling”
Notes: Here are two prior source throttling works that we will compare to in our evaluations.
The first work by Nychis et al. proposes source throttling for bufferless NoCs.
In particular, they propose an application-aware throttling based on starvation rate, which is metric they use to make throttling decision.
However, their mechanism does not adaptively adjust throttling rate based on network load.
We will call this work heterogeneous throttling for short in the evaluation section
The second work by thottethodi proposes source throttling for off-chip
It dynamically triggers throttling based on buffer occupancy.
One disadvantage of this work is that it is not app-aware, and it fully blocks packet injections of every node
Although it’s not originally designed for NoC, we still adapt it to NoC for comparison.
We will call this work self-tuned for short in the eval section.

## Slide 172: Outline
Background and Motivation
Mechanism
Prior Works
Results
Notes: Now let’s take a look at our results

## Slide 173: Methodology
Chip Multiprocessor Simulator
  64-node multi-core systems with a 2D-mesh topology
  Closed-loop core/cache/NoC cycle-level model
  64KB L1, perfect L2 (always hits to stress NoC)
Router Designs
  Virtual-channel buffered router: 4 VCs, 4 flits/VC [Dally+ IEEE TPDS’92]
  Bufferless deflection routers: BLESS [Moscibroda+ ISCA’09]
Workloads
  60 multi-core workloads: SPEC CPU2006 benchmarks
  Categorized based on their network intensity
    Low/Medium/High intensity categories
Metrics: Weighted Speedup (perf.), perf./Watt (energy eff.), and maximum slowdown (fairness)
Notes: Here is our methodology.
We simulate 64-node multi-core systems …
The CPU cores model stalls, and interact with the caches and network in a closed-loop way.
We eval our throttling mechanism on top of different router designs.
1.
We form 60 multi-core workloads using spec
For measuring performance, we use weighted speedup which has been shown to a good multicore throughput metric

## Slide 174: Performance: Bufferless NoC (BLESS)
Chart: Workload Categories
| HL | HML | HM | H | amean
BLESS | 39.5123 | 38.9303 | 25.2614 | 15.0946 | 29.2127
Hetero. | 40.5786 | 40.1135 | 26.1258 | 15.3219 | 30.0343
HAT | 43.2522 | 43.3974 | 28.1143 | 16.3917 | 32.2514
HAT provides better performance improvement than past work
Highest improvement on heterogeneous workload mixes
- L and M are more sensitive to network latency
7.4%
Notes: We will first present performance results on BUFFERLESS NOCs USING BLESS
Y-axis
X-axis different workload categories, each category contains 15 wklds
In each bar group, the blue bar is for the baseline system without any throttling.
The second red bar uses heterogeneous throttling proposed by Nychis et al..
The last green bar is HAT.
Sevaral observations can be made:
First, HAT CONSISTENLY provides…BLUE. On average it achieve 7.4% performance improvement over hetero.
Second, GREEN
b/c L & M intensity applications are more sensitive to network latency and can benefit more from reduced congestion.

## Slide 175: Performance: Buffered NoC
Chart: Workload Categories
| HL | HML | HM | H | amean
Buffered | 43.4324 | 42.8599 | 30.7187 | 20.7078 | 33.8653
Self-Tuned | 43.3173 | 42.7665 | 29.9213 | 20.454 | 33.5555
Hetero. | 43.7044 | 43.061 | 30.6928 | 20.9577 | 34.0367
HAT | 44.8544 | 44.8571 | 32.3874 | 20.9946 | 35.1869
Congestion is much lower in Buffered NoC, but HAT still provides performance benefit
+ 3.5%
Notes: Here we show the performance on buffered network.
In addition to HAT and hetero., we also show perf of self-tuned by thottethodi
We see similar perf trend as in bufferless noc. HAT consistently provides higher perf improvement over the previous designs
BLUE  3.5%
3. Little gain for self-tuned b/c it performs hard throttling by completely blocking traffic injection until congestion is cleared.
This will only temporarily reduces congestion, but congestion will return soon once packet injections are allowed again.

## Slide 176: Application Fairness
HAT provides better fairness than prior works
Chart: Normalized Maximum Slowdwon
| amean
BLESS | 1
Hetero. | 1.1176
HAT | 0.85144
Chart: 
| amean
Buffered | 1
Self-Tuned | 1.0066
Hetero. | 0.9967
HAT | 0.95261
- 15%
- 5%
Notes: Next we show that HAT does not unfairly penalize any application through throttling
By reducing congestion in the network, HAT is actually able to improve performance of maximum slowed down application.

## Slide 177: Network Energy Efficiency
Chart: Normalized Perf. per Wat
| BLESS | Buffered
Baseline | 1 | 1
HAT | 1.085 | 1.05
8.5%
5%
HAT increases energy efficiency by reducing congestion
Notes: In addition, we evaluate HAT’s effect on network energy efficiency
Y:
X:
We use an improved ORION power model to evaluate static and dynamic power consumed by the on-chip network.
On average, HAT increases energy efficiency by 8.5% and 5% for BLESS and buffered networks, respectively.
This is because HAT allows packets to traverse through the network more quickly with less congestion.
X: HAT shows better improvement on BLESS because dynamic power dominated the total power due to higher deflection rate.

## Slide 178: Other Results in Paper
Performance on CHIPPER
Performance on multithreaded workloads
Parameters sensitivity sweep of HAT
Notes: Here’s a highlight of other results in the paper.
We evaluate the performance of different throttling works on another bufferless router design called CHIPPER.

## Slide 179: Conclusion
Problem: Packets contend in on-chip networks (NoCs), causing congestion, thus reducing performance
Observations:
1) Some applications are more sensitive to network latency than others 2) Applications must be throttled differently to achieve peak performance
Key Idea: Heterogeneous Adaptive Throttling (HAT) 1) Application-aware source throttling 2) Network-load-aware throttling rate adjustment
Result: Improves performance and energy efficiency over state-of-the-art source throttling policies
Notes: In conclusion,
We address the problem of network congestion.
We make two key observations in this work:
First, some apps are more sen to network latency than others
Second, apps ……
Based on these two key observations, we propose our source throttling mechanism called HAT, which has two key components:
First, HAT performs app-aware source throttling, which selectively throttles certain applications.
Second, HAT dynamically adjusts throttling rate based on network load to achieve good performance.
Our evaluation shows that HAT improves perf…..

## Slide 180: Application-Aware Packet Scheduling
  Reetuparna Das, Onur Mutlu, Thomas Moscibroda, and Chita R. Das, "Application-Aware Prioritization Mechanisms for On-Chip Networks" Proceedings of the 42nd International Symposium on Microarchitecture (MICRO), pages 280-291, New York, NY, December 2009. Slides (pptx)

## Slide 181: The Problem: Packet Scheduling
Network-on-Chip
L2$
L2$
L2$
L2$
Bank
mem cont
Memory Controller
P
Accelerator
L2$
Bank
L2$
Bank
P
P
P
P
P
P
P
On-chip Network
App1
App2
App N+1
App N
On-chip Network is a critical resource
shared by multiple applications

## Slide 182
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Routers
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
The Problem: Packet Scheduling
182

## Slide 183
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
VC
1
VC
2
From East
From West
From North
From South
From PE
The Problem: Packet Scheduling
183

## Slide 184
The Problem: Packet Scheduling
184
Conceptual
View
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
VC
1
VC
2
From East
From West
From North
From South
From PE
Allocator
(SA)

## Slide 185
The Problem: Packet Scheduling
185
Scheduler
Conceptual
View
VC
0
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)
VC
1
VC
2
From East
From West
From North
From South
From PE
From East
From West
From North
From South
From PE
VC 0
VC 1
VC 2
App1
App2
App3
App4
App5
App6
App7
App8
Which packet to choose?

## Slide 186: The Problem: Packet Scheduling
Existing scheduling policies
  Round Robin
  Age
Problem 1: Local to a router
  Lead to contradictory decision making between routers: packets from one application may be prioritized at one router, to be delayed at next.
Problem 2: Application oblivious
  Treat all applications packets equally
  But applications are heterogeneous
Solution: Application-aware global scheduling policies.

## Slide 187: Motivation: Stall-Time Criticality
Applications are not homogenous
Applications have different criticality with respect to the network
  Some applications are network latency sensitive
  Some applications are network latency tolerant
Application’s Stall Time Criticality (STC) can be measured by its average network stall time per packet (i.e. NST/packet)
  Network Stall Time (NST) is number of cycles the processor stalls waiting for network transactions to complete

## Slide 188: Motivation: Stall-Time Criticality
Why do applications have different network stall time criticality (STC)?
  Memory Level Parallelism (MLP)
    Lower MLP leads to higher criticality
  Shortest Job First Principle (SJF)
    Lower network load leads to higher criticality

## Slide 189: STC Principle 1: MLP
Observation 1: Packet Latency != Network Stall Time
STALL
STALL
STALL of Red Packet = 0
LATENCY
LATENCY
LATENCY
Application with high MLP
Compute

## Slide 190: STC Principle 1: MLP
Observation 1: Packet Latency != Network Stall Time
Observation 2: A low MLP application’s packets have higher criticality than a high MLP application’s
STALL
STALL
STALL of Red Packet = 0
LATENCY
LATENCY
LATENCY
Application with high MLP
Compute
STALL
LATENCY
STALL
LATENCY
STALL
LATENCY
Application with low MLP

## Slide 191: STC Principle 2: Shortest-Job-First
4X network slow down
1.2X network slow down
1.3X network slow down
1.6X network slow down
Overall system throughput (weighted speedup) increases by 34%
Running ALONE
Baseline (RR) Scheduling
SJF Scheduling
Light Application
Heavy Application

## Slide 192: Solution: Application-Aware Policies
Idea
  Identify critical applications (i.e. network sensitive applications) and prioritize their packets in each router.
Key components of scheduling policy:
  Application Ranking
  Packet Batching
Propose low-hardware complexity solution

## Slide 193: Component 1: Ranking
Ranking distinguishes applications based on Stall Time Criticality (STC)
Periodically rank applications based on STC
Explored many heuristics for estimating STC
  Heuristic based on outermost private cache Misses Per Instruction (L1-MPI) is the most effective
  Low L1-MPI => high STC => higher rank
Why Misses Per Instruction (L1-MPI)?
  Easy to Compute (low complexity)
  Stable Metric (unaffected by interference in network)

## Slide 194: Component 1 : How to Rank?
Execution time is divided into fixed “ranking intervals”
  Ranking interval is 350,000 cycles
At the end of an interval, each core calculates their L1-MPI and sends it to the Central Decision Logic (CDL)
  CDL is located in the central node of mesh
CDL forms a rank order and sends back its rank to each core
  Two control packets per core every ranking interval
Ranking order is a “partial order”
Rank formation is not on the critical path
  Ranking interval is significantly longer than rank computation time
  Cores use older rank values until new ranking is available

## Slide 195: Component 2: Batching
Problem: Starvation
  Prioritizing a higher ranked application can lead to starvation of lower ranked application
Solution: Packet Batching
  Network packets are grouped into finite sized batches
  Packets of older batches are prioritized over younger batches
Time-Based Batching
  New batches are formed in a periodic, synchronous manner across all nodes in the network, every T cycles

## Slide 196: Putting it all together: STC Scheduling Policy
Before injecting a packet into the network, it is tagged with
  Batch ID (3 bits)
  Rank ID (3 bits)
Three tier priority structure at routers
  Oldest batch first (prevent starvation)
  Highest rank first (maximize performance)
  Local Round-Robin (final tie breaker)
Simple hardware support: priority arbiters
Global coordinated scheduling
  Ranking order and batching order are same across all routers

## Slide 197: STC Scheduling Example
4
8
5
1
7
2
1
6
2
1
3
Router
Scheduler
Injection Cycles
1
2
3
4
5
6
7
8
2
2
3
Batch 2
Batch 1
Batch 0
Applications

## Slide 198: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
3
2
8
7
6
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age |  |  |  | 
STC |  |  |  | 
Time

## Slide 199: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
5
4
3
1
2
2
3
2
8
7
6
Age
3
3
5
4
6
7
8
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age | 4 | 6 | 11 | 7.0
STC |  |  |  | 
Time
Time

## Slide 200: STC Scheduling Example
4
8
5
1
7
3
2
6
2
2
3
Router
Scheduler
Round Robin
5
4
3
1
2
2
3
2
8
7
6
Age
2
3
3
5
4
6
7
8
1
2
2
STC
3
5
4
6
7
8
STALL CYCLES |  |  |  | Avg
RR | 8 | 6 | 11 | 8.3
Age | 4 | 6 | 11 | 7.0
STC | 1 | 3 | 11 | 5.0
Time
Time
Time
Rank order

## Slide 201: STC Evaluation Methodology
64-core system
  x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  32KB private L1 and 1MB per core shared L2 caches, 32 miss buffers
  4GB DRAM, 320 cycle access latency, 4 on-chip DRAM controllers
Detailed Network-on-Chip model
  2-stage routers (with speculation and look ahead routing)
  Wormhole switching (8 flit data packets)
  Virtual channel flow control (6 VCs, 5 flit buffer depth)
  8x8 Mesh (128 bit bi-directional channels)
Benchmarks
  Multiprogrammed scientific, server, desktop workloads (35 applications)
  96 workload combinations

## Slide 202: Comparison to Previous Policies
Round Robin & Age (Oldest-First)
  Local and application oblivious
  Age is biased towards heavy applications
    heavy applications flood the network
    higher likelihood of an older packet being from heavy application
Globally Synchronized Frames (GSF) [Lee et al., ISCA 2008]
  Provides bandwidth fairness at the expense of system performance
  Penalizes heavy and bursty applications
    Each application gets equal and fixed quota of flits (credits) in each batch.
    Heavy application quickly run out of credits after injecting into all active batches & stalls until oldest batch completes and frees up fresh credits.
    Underutilization of network resources

## Slide 203: STC System Performance and Fairness
9.1% improvement in weighted speedup over the best existing policy (averaged across 96 workloads)
Chart: Normalized System Speedup
| weighted
LocalRR | 1
LocalAge | 1.0015
GSF | 0.88571
STC | 1.0922
Chart: Network Unfairness
| unfairness
LocalRR | 8.646
LocalAge | 7.6077
GSF | 8.4794
STC | 7.0747

## Slide 204: Enforcing Operating System Priorities
Existing policies cannot enforce operating system (OS) assigned priorities in Network-on-Chip
Proposed framework can enforce OS assigned priorities
  Weight of applications => Ranking of applications
  Configurable batching interval based on application weight
Chart: Network Slowdown
| LocalRR | LocalAge | GSF | STC
xalan-1 | 3.5638 | 3.8025 | 18.3575 | 9.56
xalan-2 | 3.8175 | 3.8562 | 9.5 | 8.56
xalan-3 | 3.6738 | 3.875 | 5.6763 | 7.01
xalan-4 | 3.6775 | 3.8925 | 4.2938 | 6.42
xalan-5 | 3.9562 | 3.7975 | 3.0987 | 4.3
xalan-6 | 3.8775 | 3.7437 | 2.4638 | 3.8
xalan-7 | 3.9675 | 3.6337 | 2.0362 | 2.34
xalan-8 | 4.0088 | 3.7125 | 1.8563 | 1.2888
Chart: Network Slowdown
| LocalRR | LocalAge | GSF-1-2-2-8 | STC-1-2-2-8
xalan-weight-1 | 3.6545 | 3.7198 | 10.755 | 15.9475
leslie-weight-2 | 8.5606 | 6.9358 | 19.2566 | 5.205
lbm-weight-2 | 4.3396 | 4.8143 | 15.2905 | 5.9969
tpcw-weight-8 | 6.0661 | 4.681 | 3.2729 | 2.0325
W. Speedup 0.49 0.49 0.46 0.52
W. Speedup 0.46 0.44 0.27 0.43

## Slide 205: Application Aware Packet Scheduling: Summary
Packet scheduling policies critically impact performance and fairness of NoCs
Existing packet scheduling policies are local and application oblivious
STC is a new, global, application-aware approach to packet scheduling in NoCs
  Ranking: differentiates applications based on their criticality
  Batching: avoids starvation due to rank-based prioritization
Proposed framework
  provides higher system performance and fairness than existing policies
  can enforce OS assigned priorities in network-on-chip

## Slide 206: Slack-Driven Packet Scheduling
  Reetuparna Das, Onur Mutlu, Thomas Moscibroda, and Chita R. Das, "Aergia: Exploiting Packet Latency Slack in On-Chip Networks" Proceedings of the 37th International Symposium on Computer Architecture (ISCA), pages 106-116, Saint-Malo, France, June 2010. Slides (pptx)

## Slide 207: Packet Scheduling in NoC
Existing scheduling policies
  Round robin
  Age
Problem
  Treat all packets equally
  Application-oblivious
Packets have different criticality
  Packet is critical if latency of a packet affects application’s performance
  Different criticality due to memory level parallelism (MLP)
All packets are not the same…!!!
Notes: There are two existing scheduling policies
RR {explain}
Age {explain}
  Lead to contradictory decision making between routers: packets from one application may be prioritized at one router, to be delayed at next.
Stress bullets of application-oblivious
Transition:
Lets look at the motivation behind our proposed application-aware policies

## Slide 208: MLP Principle
Latency ( )
Stall
Compute
Latency ( )
Latency ( )
Stall ( ) = 0
Packet Latency != Network Stall Time
Different Packets have different criticality due to MLP
Criticality( ) >
Criticality( ) >
Criticality( )
Notes: with MLP cores issue several memory requests in parallel in the hope of overlapping future load misses with current load misses.
First I show an application with high MLP, it does some computation and sends a bunch of packets(in this case three, green, blue, red).
The core stalls for the packets to return.
Note that blue packet’s latency is overlapped and hence it has much fewer stall cycles.
Stall cycles of red packet is 0 because its latency is completely overlapped.
Thus our first observation packet latency != NST and different packets have different stalll / impact on execution time

## Slide 209: Outline
Introduction
  Packet Scheduling
  Memory Level Parallelism
Aérgia
  Concept of Slack
  Estimating Slack
Evaluation
Conclusion

## Slide 210: What is Aérgia?
Aérgia is the spirit of laziness in Greek mythology
Some packets can afford to slack!

## Slide 211: Outline
Introduction
  Packet Scheduling
  Memory Level Parallelism
Aérgia
  Concept of Slack
  Estimating Slack
Evaluation
Conclusion

## Slide 212: Slack of Packets
What is slack of a packet?
  Slack of a packet is number of cycles it can be delayed in a router without (significantly) reducing application’s performance
  Local network slack
Source of slack: Memory-Level Parallelism (MLP)
  Latency of an application’s packet hidden from application due to overlap with latency of pending cache miss requests
Prioritize packets with lower slack

## Slide 213: Concept of Slack
Instruction
Window
Stall
Network-on-Chip
Load Miss
Causes
returns earlier than necessary
Compute
Slack ( ) = Latency ( ) – Latency ( ) = 26 – 6 = 20 hops
Execution Time
Packet( ) can be delayed for available slack cycles without reducing performance!
Causes
Load Miss
Latency ( )
Latency ( )
Slack
Slack
Notes: We have two cores, core A colored green and core B colored red

## Slide 214: Prioritizing using Slack
Core A
Core B
Packet | Latency | Slack
 | 13 hops | 0 hops
 | 3 hops | 10 hops
 | 10 hops | 0 hops
 | 4 hops | 6 hops
Causes
Causes
Load Miss
Load Miss
Prioritize
Load Miss
Load Miss
Causes
Causes
Interference at 3 hops
Slack( ) > Slack ( )
Notes: Now the packets B-1 and A-0 interfere in the network for 3 hops, and we can choose one over the other
A-0 has slack of 0 hops and B-1 has a slack of 6 hops
So we can Prioritize A-0 over B-1 to reduce stall cycles of Core-A without increasing stall cycles of Core-B

## Slide 215: Slack in Applications
Chart: Slack in cycles
| 0.0 | 50.0 | 100.0 | 150.0 | 200.0 | 250.0 | 300.0 | 350.0 | 400.0 | 450.0 | 500.0
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
50% of packets have 350+ slack cycles
10% of packets have <50 slack cycles
Non-critical
critical

## Slide 216: Slack in Applications
Chart: Slack in cycles
| 0.0 | 50.0 | 100.0 | 150.0 | 200.0 | 250.0 | 300.0 | 350.0 | 400.0 | 450.0 | 500.0
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
art | 67.34 | 78.35 | 86.47 | 91.15 | 93.69 | 95.3 | 96.4 | 97.21 | 97.89 | 98.49 | 98.96
68% of packets have zero slack cycles

## Slide 217: Diversity in Slack
Chart: Slack in cycles
| 0.0 | 50.0 | 100.0 | 150.0 | 200.0 | 250.0 | 300.0 | 350.0 | 400.0 | 450.0 | 500.0
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
omnet | 18.26 | 22.6 | 27.38 | 31.83 | 35.94 | 39.76 | 43.34 | 46.76 | 50.07 | 53.29 | 56.34
tpcw | 24.84 | 32.69 | 39.43 | 43.74 | 47.01 | 49.78 | 52.44 | 55.46 | 59.42 | 64.22 | 68.83
mcf | 20.8 | 22.89 | 25.4 | 27.69 | 29.83 | 31.93 | 34.03 | 36.17 | 38.44 | 40.85 | 43.29
bzip2 | 16.61 | 26.43 | 43.7 | 52.13 | 57.33 | 61.22 | 64.5 | 67.73 | 71.62 | 75.76 | 79.07
sjbb | 31.97 | 44.81 | 54.63 | 59.02 | 61.71 | 63.81 | 65.95 | 69.02 | 74.12 | 80.2 | 84.77
sap | 20.91 | 33.4 | 44.4 | 49.94 | 53.68 | 56.65 | 59.47 | 62.87 | 67.63 | 73.04 | 77.64
sphinx | 33.8 | 46.89 | 57 | 62.2 | 65.55 | 68.25 | 70.75 | 73.51 | 77.02 | 81.17 | 84.85
deal | 48.38 | 63.98 | 81.27 | 87.3 | 89.68 | 91.16 | 92.32 | 93.4 | 94.56 | 95.75 | 96.79
barnes | 32.96 | 46.61 | 59.39 | 63.48 | 66.27 | 68.54 | 70.7 | 73.35 | 78.04 | 83.37 | 86.99
astar | 43.04 | 58.09 | 71.63 | 76.95 | 79.84 | 81.87 | 83.49 | 85.5 | 88.22 | 91.38 | 94.29
calculix | 55.87 | 78.45 | 90.5 | 91.95 | 92.54 | 93 | 93.43 | 93.89 | 94.58 | 95.4 | 96.12

## Slide 218: Diversity in Slack
Chart: Slack in cycles
| 0.0 | 50.0 | 100.0 | 150.0 | 200.0 | 250.0 | 300.0 | 350.0 | 400.0 | 450.0 | 500.0
Gems | 7.77 | 11.03 | 17.64 | 26.5 | 33.62 | 40.14 | 45.64 | 50.6 | 55.66 | 60.53 | 64.68
omnet | 18.26 | 22.6 | 27.38 | 31.83 | 35.94 | 39.76 | 43.34 | 46.76 | 50.07 | 53.29 | 56.34
tpcw | 24.84 | 32.69 | 39.43 | 43.74 | 47.01 | 49.78 | 52.44 | 55.46 | 59.42 | 64.22 | 68.83
mcf | 20.8 | 22.89 | 25.4 | 27.69 | 29.83 | 31.93 | 34.03 | 36.17 | 38.44 | 40.85 | 43.29
bzip2 | 16.61 | 26.43 | 43.7 | 52.13 | 57.33 | 61.22 | 64.5 | 67.73 | 71.62 | 75.76 | 79.07
sjbb | 31.97 | 44.81 | 54.63 | 59.02 | 61.71 | 63.81 | 65.95 | 69.02 | 74.12 | 80.2 | 84.77
sap | 20.91 | 33.4 | 44.4 | 49.94 | 53.68 | 56.65 | 59.47 | 62.87 | 67.63 | 73.04 | 77.64
sphinx | 33.8 | 46.89 | 57 | 62.2 | 65.55 | 68.25 | 70.75 | 73.51 | 77.02 | 81.17 | 84.85
deal | 48.38 | 63.98 | 81.27 | 87.3 | 89.68 | 91.16 | 92.32 | 93.4 | 94.56 | 95.75 | 96.79
barnes | 32.96 | 46.61 | 59.39 | 63.48 | 66.27 | 68.54 | 70.7 | 73.35 | 78.04 | 83.37 | 86.99
astar | 43.04 | 58.09 | 71.63 | 76.95 | 79.84 | 81.87 | 83.49 | 85.5 | 88.22 | 91.38 | 94.29
calculix | 55.87 | 78.45 | 90.5 | 91.95 | 92.54 | 93 | 93.43 | 93.89 | 94.58 | 95.4 | 96.12
Slack varies between packets of different applications
Slack varies between packets of a single application

## Slide 219: Outline
Introduction
  Packet Scheduling
  Memory Level Parallelism
Aérgia
  Concept of Slack
  Estimating Slack
Evaluation
Conclusion

## Slide 220: Estimating Slack Priority
Slack (P) = Max (Latencies of P’s Predecessors) – Latency of P
  Predecessors(P) are the packets of outstanding cache miss requests when P is issued
Packet latencies not known when issued
Predicting latency of any packet Q
  Higher latency if Q corresponds to an L2 miss
  Higher latency if Q has to travel farther number of hops
Notes: Difficult to predict packet latency
Predicting Max (Predecessors’ Latencies)
  Number of predecessors
  Higher predecessor latency if predecessor is L2 miss
Predicting latency of a packet P
  Higher latency if P corresponds to an L2 miss
  Higher latency if P has to travel farther number of hops

## Slide 221: Estimating Slack Priority
Slack of P = Maximum Predecessor Latency – Latency of P
Slack(P) =
  PredL2: Set if any predecessor packet is servicing L2 miss
  MyL2: Set if P is NOT servicing an L2 miss
  HopEstimate: Max (# of hops of Predecessors) – hops of P
PredL2
(2 bits)
MyL2
(1 bit)
HopEstimate
(2 bits)

## Slide 222: Estimating Slack Priority
How to predict L2 hit or miss at core?
  Global Branch Predictor based L2 Miss Predictor
    Use Pattern History Table and 2-bit saturating counters
  Threshold based L2 Miss Predictor
    If #L2 misses in “M” misses >= “T” threshold then next load is a L2 miss.
Number of miss predecessors?
  List of outstanding L2 Misses
Hops estimate?
  Hops => ∆X + ∆ Y distance
  Use predecessor list to calculate slack hop estimate

## Slide 223: Starvation Avoidance
Problem: Starvation
  Prioritizing packets can lead to starvation of lower priority packets
Solution: Time-Based Packet Batching
  New batches are formed at every T cycles
  Packets of older batches are prioritized over younger batches

## Slide 224: Putting it all together
Tag header of the packet with priority bits before injection
Priority(P)?
  P’s batch (highest priority)
  P’s Slack
  Local Round-Robin (final tie breaker)
PredL2
(2 bits)
MyL2
(1 bit)
HopEstimate
(2 bits)
Batch
(3 bits)
Priority (P) =
Notes: Say “older batches are prioritized over younger batches”

## Slide 225: Outline
Introduction
  Packet Scheduling
  Memory Level Parallelism
Aérgia
  Concept of Slack
  Estimating Slack
Evaluation
Conclusion

## Slide 226: Evaluation Methodology
64-core system
  x86 processor model based on Intel Pentium M
  2 GHz processor, 128-entry instruction window
  32KB private L1 and 1MB per core shared L2 caches, 32 miss buffers
  4GB DRAM, 320 cycle access latency, 4 on-chip DRAM controllers
Detailed Network-on-Chip model
  2-stage routers (with speculation and look ahead routing)
  Wormhole switching (8 flit data packets)
  Virtual channel flow control (6 VCs, 5 flit buffer depth)
  8x8 Mesh (128 bit bi-directional channels)
Benchmarks
  Multiprogrammed scientific, server, desktop workloads (35 applications)
  96 workload combinations
Notes: We do our evaluations on a detailed cycle accurate CMP simulator with state-of-art NoC model.
Our evaluations are across 35 diverse applications.
Our results are for 96 workload combinations.

## Slide 227: Qualitative Comparison
Round Robin & Age
  Local and application oblivious
  Age is biased towards heavy applications
Globally Synchronized Frames (GSF) [Lee et al., ISCA 2008]
  Provides bandwidth fairness at the expense of system performance
  Penalizes heavy and bursty applications
Application-Aware Prioritization Policies (SJF) [Das et al., MICRO 2009]
  Shortest-Job-First Principle
  Packet scheduling policies which prioritize network sensitive applications which inject lower load
Notes:     Age
    heavy applications flood the network
    higher likelihood of an older packet being from heavy application
GSF
    Each application gets equal and fixed quota of flits (credits) in each batch.
    Heavy application quickly run out of credits after injecting into all active batches & stall till oldest batch completes and frees up fresh credits.
    Underutilization of network resources

## Slide 228: System Performance
SJF provides 8.9% improvement in weighted speedup
Aérgia improves system throughput by 10.3%
Aérgia+SJF improves system throughput by 16.1%
Chart: Normalized System Speedup
Age | 1
RR | 1.0046
GSF | 0.88979
SJF | 1.0949
Aergia | 1.1084
SJF+Aergia | 1.1668

## Slide 229: Network Unfairness
SJF does not imbalance network fairness
Aergia improves network unfairness by 1.5X
SJF+Aergia improves network unfairness by 1.3X
Chart: Network Unfairness
Age | 10.21
RR | 10.64
GSF | 10.4794
SJF | 9.8747
Aergia | 6.78
SJF+Aergia | 7.9

## Slide 230: Conclusions & Future Directions
Packets have different criticality, yet existing packet scheduling policies treat all packets equally
We propose a new approach to packet scheduling in NoCs
  We define Slack as a key measure that characterizes the relative importance of a packet.
  We propose Aérgia a novel architecture to accelerate low slack critical packets
Result
  Improves system performance: 16.1%
  Improves network fairness: 30.8%

## Slide 231: Express-Cube Topologies
  Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Express Cube Topologies for On-Chip Interconnects" Proceedings of the 15th International Symposium on High-Performance Computer Architecture (HPCA), pages 163-174, Raleigh, NC, February 2009. Slides (ppt)

## Slide 232: 2-D Mesh

## Slide 233: 2-D Mesh
Pros
  Low design & layout complexity
  Simple, fast routers
Cons
  Large diameter
  Energy & latency impact

## Slide 234: Concentration (Balfour & Dally, ICS ‘06)
Pros
  Multiple terminals attached to a router node
  Fast nearest-neighbor communication via the crossbar
  Hop count reduction proportional to concentration degree
Cons
  Benefits limited by crossbar complexity

## Slide 235: Concentration
Side-effects
  Fewer channels
  Greater channel width

## Slide 236: Replication
CMesh-X2
Benefits
  Restores bisection channel count
  Restores channel width
  Reduced crossbar complexity

## Slide 237: Flattened Butterfly (Kim et al., Micro ‘07)
Objectives:
  Improve connectivity
  Exploit the wire budget

## Slide 238: Flattened Butterfly (Kim et al., Micro ‘07)

## Slide 239: Flattened Butterfly (Kim et al., Micro ‘07)

## Slide 240: Flattened Butterfly (Kim et al., Micro ‘07)

## Slide 241: Flattened Butterfly (Kim et al., Micro ‘07)

## Slide 242: Flattened Butterfly (Kim et al., Micro ‘07)
Pros
  Excellent connectivity
  Low diameter: 2 hops
Cons
  High channel count: k2/2 per row/column
  Low channel utilization
  Increased control (arbitration) complexity

## Slide 243: Multidrop Express Channels (MECS)
Objectives:
  Connectivity
  More scalable channel count
  Better channel utilization

## Slide 244: Multidrop Express Channels (MECS)

## Slide 245: Multidrop Express Channels (MECS)

## Slide 246: Multidrop Express Channels (MECS)

## Slide 247: Multidrop Express Channels (MECS)

## Slide 248: Multidrop Express Channels (MECS)

## Slide 249: Multidrop Express Channels (MECS)
Pros
  One-to-many topology
  Low diameter: 2 hops
  k channels row/column
  Asymmetric
Cons
  Asymmetric
  Increased control (arbitration) complexity

## Slide 250: Partitioning: a GEC Example
MECS
MECS-X2
Flattened
Butterfly
Partitioned
MECS

## Slide 251: Analytical Comparison
 | CMesh |  | FBfly |  | MECS | 
Network Size | 64 | 256 | 64 | 256 | 64 | 256
Radix (conctr’d) | 4 | 8 | 4 | 8 | 4 | 8
Diameter | 6 | 14 | 2 | 2 | 2 | 2
Channel count | 2 | 2 | 8 | 32 | 4 | 8
Channel width | 576 | 1152 | 144 | 72 | 288 | 288
Router inputs | 4 | 4 | 6 | 14 | 6 | 14
Router outputs | 4 | 4 | 6 | 14 | 4 | 4

## Slide 252: Experimental Methodology
Topologies | Mesh, CMesh, CMesh-X2, FBFly, MECS, MECS-X2
Network sizes | 64 & 256 terminals
Routing | DOR, adaptive
Messages | 64 & 576 bits
Synthetic traffic | Uniform random, bit complement, transpose, self-similar
PARSEC benchmarks | Blackscholes, Bodytrack, Canneal, Ferret, Fluidanimate, Freqmine, Vip, x264
Full-system config | M5 simulator, Alpha ISA, 64 OOO cores
Energy evaluation | Orion + CACTI 6

## Slide 253
64 nodes: Uniform Random

## Slide 254
256 nodes: Uniform Random

## Slide 255
Energy (100K pkts, Uniform Random)

## Slide 256
64 Nodes: PARSEC

## Slide 257: Summary
MECS
  A new one-to-many topology
  Good fit for planar substrates
  Excellent connectivity
  Effective wire utilization
Generalized Express Cubes
  Framework & taxonomy for NOC topologies
  Extension of the k-ary n-cube model
  Useful for understanding and exploring on-chip interconnect options
  Future: expand & formalize

## Slide 258: Kilo-NoC: Topology-Aware QoS
Boris Grot, Joel Hestness, Stephen W. Keckler, and Onur Mutlu, "Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees" Proceedings of the 38th International Symposium on Computer Architecture (ISCA), San Jose, CA, June 2011. Slides (pptx)

## Slide 259: Motivation
Extreme-scale chip-level integration
  Cores
  Cache banks
  Accelerators
  I/O logic
  Network-on-chip (NOC)
10-100 cores today
1000+ assets in the near future

## Slide 260: Kilo-NOC requirements
High efficiency
  Area
  Energy
Good performance
Strong service guarantees (QoS)

## Slide 261: Topology-Aware QoS
Problem: QoS support in each router is expensive (in terms of buffering, arbitration, bookkeeping)
  E.g., Grot et al., “Preemptive Virtual Clock: A Flexible, Efficient, and Cost-effective QOS Scheme for Networks-on-Chip,” MICRO 2009.
Goal: Provide QoS guarantees at low area and power cost
Idea:
  Isolate shared resources in a region of the network, support QoS within that area
  Design the topology so that applications can access the region without interference

## Slide 262: Baseline QOS-enabled CMP
Multiple VMs
sharing a die
Shared resources
(e.g., memory controllers)
VM-private resources
(cores, caches)
QOS-enabled router
Q

## Slide 263: Conventional NOC QOS
Contention scenarios:
Shared resources
  memory access
Intra-VM traffic
  shared cache access
Inter-VM traffic
  VM page sharing

## Slide 264: Conventional NOC QOS
Contention scenarios:
Shared resources
  memory access
Intra-VM traffic
  shared cache access
Inter-VM traffic
  VM page sharing
Network-wide guarantees without network-wide QOS support

## Slide 265: Kilo-NOC QOS
Insight: leverage rich network connectivity
  Naturally reduce interference among flows
  Limit the extent of hardware QOS support
Requires a low-diameter topology
  This work: Multidrop Express Channels (MECS)
  Grot et al., HPCA 2009

## Slide 266: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference
QOS-free

## Slide 267: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 268: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 269: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 270: Kilo-NOC view
Topology-aware QOS support
  Limit QOS complexity to a fraction of the die
Optimized flow control
  Reduce buffer requirements in QOS-free regions
QOS-free

## Slide 271: Evaluation Methodology
Parameter | Value
Technology | 15 nm
Vdd | 0.7 V
System | 1024 tiles: 256 concentrated nodes (64 shared resources)
Networks: | 
MECS+PVC | VC flow control, QOS support (PVC) at each node
MECS+TAQ | VC flow control, QOS support only in shared regions
MECS+TAQ+EB | EB flow control outside of SRs, Separate Request and Reply networks
K-MECS | Proposed organization: TAQ + hybrid flow control

## Slide 272: Area comparison

## Slide 273: Energy comparison

## Slide 274: Summary
Kilo-NOC: a heterogeneous NOC architecture for kilo-node substrates
Topology-aware QOS
  Limits QOS support to a fraction of the die
  Leverages low-diameter topologies
  Improves NOC area- and energy-efficiency
  Provides strong guarantees

## Slide 275: Scalable Many-Core Memory Systems Optional Topic 5: Interconnects
Prof. Onur Mutlu
http://www.ece.cmu.edu/~omutlu
onur@cmu.edu
HiPEAC ACACES Summer School 2013
July 15-19, 2013