## Slide 1: Computation in Memory An Architectural Perspective
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
20 July 2020
DAC Tutorial on Toward New Era of Compute-in-Memory

## Slide 2: The Problem
Computing
is Bottlenecked by Data

## Slide 3: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate more than we can process

## Slide 4: Data is Key for Future Workloads
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 5: Data Overwhelms Modern Machines
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Data → performance & energy bottleneck

## Slide 6
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data is Key for Future Workloads
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 7
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 8: Data is Key for Future Workloads
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 9
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Data → performance & energy bottleneck
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 10: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION

## Slide 11: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION
Data → performance & energy bottleneck

## Slide 12: Data Overwhelms Modern Machines …
Storage/memory capability
Communication capability
Computation capability
Greatly impacts robustness, energy, performance, cost

## Slide 13: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 14: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data

## Slide 15
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 16
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement
Data Movement Overwhelms Modern Machines

## Slide 17: Axiom
An Intelligent Architecture
Handles Data Well

## Slide 18: How to Handle Data Well
Ensure data does not overwhelm the components
  via intelligent algorithms
  via intelligent architectures
  via whole system designs: algorithm-architecture-devices
Take advantage of vast amounts of data and metadata
  to improve architectural & system-level decisions
Understand and exploit properties of (different) data
  to improve algorithms & architectures in various metrics

## Slide 19: Corollaries: Architectures Today …
Architectures are terrible at dealing with data
  Designed to mainly store and move data vs. to compute
  They are processor-centric as opposed to data-centric
Architectures are terrible at taking advantage of vast amounts of data (and metadata) available to them
  Designed to make simple decisions, ignoring lots of data
  They make human-driven decisions vs. data-driven decisions
Architectures are terrible at knowing and exploiting different properties of application data
  Designed to treat all data as the same
  They make component-aware decisions vs. data-aware

## Slide 20: Data-Centric (Memory-Centric) Architectures

## Slide 21: Data-Centric Architectures: Properties
Process data where it resides (where it makes sense)
  Processing in and near memory structures
Low-latency and low-energy data access
  Low latency memory
  Low energy memory
Low-cost & scalable data storage and processing
  High capacity memory at low cost: hybrid memory, compression
Intelligent data management
  Intelligent controllers handling robustness, security, cost

## Slide 22: Processing Data Where It Makes Sense

## Slide 23: Processing in/near Memory: An Old Idea
Stone, “A Logic-in-Memory Computer,” IEEE TC 1970.

## Slide 24: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures

## Slide 25: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures

## Slide 26: Memory Scaling Issues Were Real
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Proceedings of the 5th International Memory Workshop (IMW), Monterey, CA, May 2013. Slides (pptx) (pdf) EETimes Reprint
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 27: Memory Scaling Issues Are Real
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version]

## Slide 28: The Story of RowHammer
One can predictably induce bit flips in commodity DRAM chips
  >80% of the tested DRAM chips are vulnerable
First example of how a simple hardware failure mechanism can create a widespread system security vulnerability

## Slide 29: Recent DRAM Is More Vulnerable
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 30: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)

## Slide 31: The Push from Circuits and Devices
Main Memory Needs
Intelligent Controllers

## Slide 32: RowHammer in 2020 (I)
Jeremie S. Kim, Minesh Patel, A. Giray Yaglikci, Hasan Hassan, Roknoddin Azizi, Lois Orosa, and Onur Mutlu, "Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques" Proceedings of the 47th International Symposium on Computer Architecture (ISCA), Valencia, Spain, June 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 33: Key Takeaways from 1580 Chips
Chips of newer DRAM technology nodes are more vulnerable to RowHammer
There are chips today whose weakest cells fail after only 4800 hammers
Chips of newer DRAM technology nodes can exhibit RowHammer bit flips 1) in more rows and 2) farther away from the victim row.
Existing mitigation mechanisms are not effective
Notes: To reiterate our three key takeaways from our experimental characterization, we find that
[CLICK] First, chips of newer DRAM technology nodes are more vulnerable to RowHammer
[CLICK] Second, there are chips today whose weakest cells fail after only 4800 hammers
[CLICK] Third, chips of newer DRAM technology nodes can exhibit RowHammer bit flips in more rows and farther away from the victim row
================

## Slide 34: RowHammer in 2020 (II)
Pietro Frigo, Emanuele Vannacci, Hasan Hassan, Victor van der Veen, Onur Mutlu, Cristiano Giuffrida, Herbert Bos, and Kaveh Razavi, "TRRespass: Exploiting the Many Sides of Target Row Refresh" Proceedings of the 41st IEEE Symposium on Security and Privacy (S&P), San Francisco, CA, USA, May 2020. [Slides (pptx) (pdf)] [Talk Video (17 minutes)] [Source Code] [Web Article] Best paper award.

## Slide 35: The Push from Circuits and Devices
Main Memory Needs
Intelligent Controllers

## Slide 36: Data Retention in Memory [Liu et al., ISCA 2013]
Retention Time Profile of DRAM looks like this:
Location dependent
Stored value pattern dependent
Time dependent

## Slide 37: More on DRAM Refresh (I)
Jamie Liu, Ben Jaiyen, Richard Veras, and Onur Mutlu, "RAIDR: Retention-Aware Intelligent DRAM Refresh" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pdf)

## Slide 38: More on DRAM Refresh (II)
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 39: More on DRAM Refresh (III)
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 40: More on DRAM Refresh (IV)
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 41: More on DRAM Refresh (V)
Samira Khan, Donghyuk Lee, and Onur Mutlu, "PARBOR: An Efficient System-Level Technique to Detect Data-Dependent Failures in DRAM" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Toulouse, France, June 2016. [Slides (pptx) (pdf)]

## Slide 42: More on DRAM Refresh (VI)
Samira Khan, Chris Wilkerson, Zhe Wang, Alaa R. Alameldeen, Donghyuk Lee, and Onur Mutlu, "Detecting and Mitigating Data-Dependent DRAM Failures by Exploiting Current Memory Content" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 43: More on DRAM Refresh (VII)
Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "The Reach Profiler (REAPER): Enabling the Mitigation of DRAM Retention Failures via Profiling at Aggressive Conditions" Proceedings of the 44th International Symposium on Computer Architecture (ISCA), Toronto, Canada, June 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]
First experimental analysis of (mobile) LPDDR4 chips
Analyzes the complex tradeoff space of retention time profiling
Idea: enable fast and robust profiling at higher refresh intervals & temperatures

## Slide 44: More on DRAM Refresh (VIII)
Minesh Patel, Jeremie S. Kim, Hasan Hassan, and Onur Mutlu, "Understanding and Modeling On-Die Error Correction in Modern DRAM: An Experimental Study Using Real Devices" Proceedings of the 49th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Portland, OR, USA, June 2019. [Slides (pptx) (pdf)] [Talk Video (26 minutes)] [Full Talk Lecture (29 minutes)] [Source Code for EINSim, the Error Inference Simulator] Best paper award.

## Slide 45: The Push from Circuits and Devices
Main Memory Needs
Intelligent Controllers

## Slide 46: Industry Is Writing Papers About It, Too

## Slide 47: Call for Intelligent Memory Controllers

## Slide 48: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
Pull from Systems and Applications
  Data access is a major system and application bottleneck
  Systems are energy limited
  Data movement much more energy-hungry than computation

## Slide 49: Three Key Systems Trends
1. Data access is a major bottleneck
  Applications are increasingly data hungry
2. Energy consumption is a key limiter
3. Data movement energy dominates compute
  Especially true for off-chip to on-chip movement

## Slide 50: Do We Want This?
Source: V. Milutinovic

## Slide 51: Or This?
Source: V. Milutinovic

## Slide 52: Challenge and Opportunity for Future
High Performance,
Energy Efficient,
Sustainable

## Slide 53: The Problem
Data access is the major performance and energy bottleneck
Our current
design principles
cause great energy waste
(and great performance loss)

## Slide 54: The Problem
Processing of data
is performed
far away from the data

## Slide 55: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 56: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 57: Today’s Computing Systems
Are overwhelmingly processor centric
All data processed in the processor  at great system cost
Processor is heavily optimized and is considered the master
Data storage units are dumb and are largely unoptimized (except for some that are on the processor die)

## Slide 58: Yet …
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 59: The Performance Perspective
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors" Proceedings of the 9th International Symposium on High-Performance Computer Architecture (HPCA), pages 129-140, Anaheim, CA, February 2003. Slides (pdf)

## Slide 60: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 61: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 62: Perils of Processor-Centric Design
Grossly-imbalanced systems
  Processing done only in one place
  Everything else just stores and moves data: data moves a lot
   Energy inefficient
   Low performance
   Complex
Overly complex and bloated processor (and accelerators)
  To tolerate data access from memory
  Complex hierarchies and mechanisms
   Energy inefficient
   Low performance
   Complex

## Slide 63: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data

## Slide 64: The Energy Perspective
Dally, HiPEAC 2015

## Slide 65: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 66: Data Movement vs. Computation Energy
Data movement is a major system energy bottleneck
  Comprises 41% of mobile system energy during web browsing [2]
  Costs ~115 times as much energy as an ADD operation [1, 2]
[1]: Reducing data Movement Energy via Online Data Clustering and Encoding (MICRO’16)
[2]: Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms (IISWC’14)

## Slide 67: Energy Waste in Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 68: We Do Not Want to Move Data!
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 69: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 70: Goal: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processor chip and in-memory units?
  software and hardware interfaces?
  system software, compilers, languages?
  algorithms and theoretical foundations?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 71: Processing in Memory: Two Approaches
1. Minimally changing memory chips
2. Exploiting 3D-stacked memory

## Slide 72: Approach 1: Minimally Changing Memory
DRAM has great capability to perform bulk data movement and computation internally with small changes
  Can exploit internal connectivity to move data
  Can exploit analog computation capability
  …
Examples: RowClone, In-DRAM AND/OR, Gather/Scatter DRAM
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)
  "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology” (Seshadri et al., MICRO 2017)

## Slide 73: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 74: Today’s Systems: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 75: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 76: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 77: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 78: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 79: Memory as an Accelerator
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 80: In-Memory Bulk Bitwise Operations
We can support in-DRAM COPY, ZERO, AND, OR, NOT, MAJ
At low cost
Using analog computation capability of DRAM
  Idea: activating multiple rows performs computation
30-60X performance and energy improvement
  Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
New memory technologies enable even more opportunities
  Memristors, resistive RAM, phase change mem, STT-MRAM, …
  Can operate on data with minimal movement

## Slide 81: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 82: In-DRAM Bulk Bitwise AND/OR Operation
BULKAND A, B  C
Semantics: Perform a bitwise AND of two rows A and B and store the result in row C
R0 – reserved zero row, R1 – reserved one row
D1, D2, D3 – Designated rows for triple activation
1. RowClone A into D1
2. RowClone B into D2
3. RowClone R0 into D3
4. ACTIVATE D1,D2,D3
5. RowClone Result into C

## Slide 83: In-DRAM NOT: Dual Contact Cell
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
Idea:
Feed the
negated value
in the sense amplifier
into a special row

## Slide 84: Ambit vs. DDR3: Performance and Energy
Chart: 
| not | and/or | nand/nor | xor/xnor | mean
Performance Improvement | 51.6251 | 38.3193 | 30.6965 | 21.8566 | 32
Energy Reduction | 59.5 | 43.9 | 35.1 | 25.1 | 35
32X
35X
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 85: Bulk Bitwise Operations in Workloads
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017

## Slide 86: Performance: Bitmap Index on Ambit
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>5.4-6.6X Performance Improvement

## Slide 87: Performance: BitWeaving on Ambit
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 88: More on In-DRAM Bulk AND/OR
Vivek Seshadri, Kevin Hsieh, Amirali Boroumand, Donghyuk Lee, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Fast Bulk Bitwise AND and OR in DRAM" IEEE Computer Architecture Letters (CAL), April 2015.

## Slide 89: More on In-DRAM Bitwise Operations
Vivek Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.

## Slide 90: More on In-DRAM Bulk Bitwise Execution
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]

## Slide 91: RowClone & Bitwise Ops in Real DRAM Chips
https://parallel.princeton.edu/papers/micro19-gao.pdf

## Slide 92: Pinatubo: RowClone and Bitwise Ops in PCM
https://cseweb.ucsd.edu/~jzhao/files/Pinatubo-dac2016.pdf

## Slide 93: Processing in Memory: Two Approaches
1. Minimally changing memory chips
2. Exploiting 3D-stacked memory

## Slide 94: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 95: DRAM Landscape (circa 2015)
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.

## Slide 96: Two Key Questions in 3D-Stacked PIM
What are the performance and energy benefits of using 3D-stacked memory as a coarse-grained accelerator?
  By changing the entire system
  By performing simple function offloading
What is the minimal processing-in-memory support we can provide?
  With minimal changes to system and programming

## Slide 97: Graph Processing
Large graphs are everywhere (circa 2015)
Scalable large-scale graph processing is challenging
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos
Chart: Speedup
| 128 Cores | 32 Cores
열3 | 1.4206 | 1

## Slide 98: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 99: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 100: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communications via Remote Function Calls

## Slide 101: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 102: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
Tesseract
32 Tesseract Cores
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 103: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
On five graph processing algorithms

## Slide 104: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
Chart: Memory Bandwidth Consumption
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 0.079545 | 0.1904 | 0.24289 | 1.2943 | 2.244 | 2.9197

## Slide 105: Tesseract Graph Processing System Energy
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
> 8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 106: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 107: Two Key Questions in 3D-Stacked PIM
What are the performance and energy benefits of using 3D-stacked memory as a coarse-grained accelerator?
  By changing the entire system
  By performing simple function offloading
What is the minimal processing-in-memory support we can provide?
  With minimal changes to system and programming

## Slide 108: PIM on Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.

## Slide 109: Consumer Devices
Consumer devices are everywhere!
Energy consumption is a first-class concern in consumer devices
Notes: Consumer devices like tablets smartphone and wearable are now everywhere and used by billions of people.
One of the major challenge in these devices is battery limitation which makes the energy consumption a critical concern …

## Slide 110: Popular Google Consumer Workloads
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 111: Energy Cost of Data Movement
Data Movement
1st key observation: 62.7% of the total system energy is spent on data movement
  Potential solution: move computation close to data
  Challenge: limited area and energy budget
Processing-In-Memory (PIM)
SoC
DRAM
L2
L1
CPU
CPU
CPU
CPU
Compute Unit
Notes: Throughout our analysis, we make a key observation that out of all sources of energy consumption, data movement is a major contributor to the total system energy. We find that across all of the workloads, on average around 62.7% of total system energy is spent on data movement.
One way to reduce data movement cost is to move computation close to data, or …
One potential solution to address this cost it do move computation close to data, or in other words, do procesing in memory. However, the challenge is that these devices.
One potential solution to mitigate data movement cost and reduce total system energy is to execute data-movement heavy portions of application close to data, or in other words, do processing in memory. However, consumer devices are extermely limited in terms of area and power budget. So the question is can we move part of the data movement heavy portion given the limited area and energy budget. Our

## Slide 112: Using PIM to Reduce Data Movement
  2nd key observation: a significant fraction of the data movement often comes from simple functions
PIM Core
PIM Accelerator
PIM Accelerator
PIM Accelerator
We can design lightweight logic to implement these simple functions in memory
Small embedded low-power core
Small fixed-function accelerators
  Offloading to PIM logic reduces energy and improves performance, on average, by 55.4% and 54.2%
Notes: To figure out if we can use processing in memory, we dig deeper into our analysis and we make another key observation that majority of data movement often comes form simple functions and pritmitives. We find that these simple function can be implemented in memory as either a small embedded core, or group of small fixed function accelerators. Our result shows that offloading these function to PIM logic can significantly reduce data movement for each function and reduce energy on average around 55% and improve perforamcne around 54%.
our PIM core can reduce significant portion of data movement, reduce enregy by 49.1% for each function and improve performance up to 2.2X. While using group of fixed function accelerator reduce energy by 55.4% and improve performance by up to 2.5X.
  Or use Saugata’s approach : Reduces total system energy by an average of 55.4%
  Reduces execution time by an average of 54.2%
Our result show that both of them can significantly reduce the data movement for each function.
Feedback: talk about result more
Don’t talk about specific detail like MemCopy, MemSet stuff like that
Main take away: data movement come from simple functions that are simple enough to implement in PIM
We find that these functions and primitves can be implemented as PIM logic using either (1) a small low-power general-purpose embedded core or (2) a group of small fixed-function accelerators (PIM accelerators). Our Analysis shows that both are cost-feasible to use in consumer devices. We find that they eliminate a significant fraction of dat amovement, and reduce energy consumption for each of these operation on average by 49 and 55%.

## Slide 113: Workload Analysis
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 114: TensorFlow Mobile
57.3% of the inference energy is spent on data movement
54.4% of the data movement energy comes from packing/unpacking and quantization
Inference
Prediction

## Slide 115: Packing
Reorders elements of matrices to minimize cache misses during matrix multiplication
Up to 40% of the inference energy and 31% of inference execution time
Packing’s data movement accounts for up to 35.3% of the inference energy
Packing
Matrix
Packed Matrix
A simple data reorganization process that requires simple arithmetic

## Slide 116: Quantization
Converts 32-bit floating point to 8-bit integers to improve inference execution time and energy consumption
Up to 16.8% of the inference energy and 16.1% of inference execution time
Majority of quantization energy comes from data movement
Quantization
floating point
integer
A simple data conversion operation that requires shift, addition, and multiplication operations

## Slide 117: Normalized Energy
Chart: Normalized Energy
| Texture Tiling | Color Blitting | Com- pression | Decom- pression | Packing | Quantization | Sub-Pixel Interpolation | Deblocking Filter | Motion Estimation
CPU-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Core | 0.41638 | 0.531 | 0.59396 | 0.40527 | 0.5087 | 0.50462 | 0.50061 | 0.49893 | 0.59594
PIM-Acc | 0.36127 | 0.42335 | 0.47294 | 0.29851 | 0.47245 | 0.42913 | 0.34481 | 0.26459 | 0.3925
Chrome Browser
Video Playback and Capture
TensorFlow Mobile
PIM core and PIM accelerator reduce energy consumption on average by 49.1% and 55.4%
Notes: We make another obsrevation that using PIM accelerator provide limited energy reduction over PIM core, for some of these workloads, such as texture tiling. This is becase these kernels are data intensive and have low ocmputational compleity, and as a result, using fixed function accelerator does not provide significant energy reduction over the PIM core.

## Slide 118: Normalized Runtime
Chart: Normalized Runtime
| Texture Tiling | Color Blitting | Comp- ression | Decomp- ression | Sub-Pixel Interpolation | Deblocking Filter | Motion Estimation | TensorFlow
CPU-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Core | 0.43478 | 0.64516 | 0.76336 | 0.76923 | 0.72464 | 0.8 | 0.84746 | 0.63694
PIM-Acc | 0.4 | 0.57803 | 0.47619 | 0.5 | 0.5814 | 0.70423 | 0.47619 | 0.50505
Chrome Browser
Video Playback and Capture
TensorFlow Mobile
Offloading these kernels to PIM core and PIM accelerator improves performance on average by 44.6% and 54.2%
Notes: PIM-Core and PIM-Acc significantly outperform CPU-Only across all kernels, improving performance by … This perfomance benefit come from higher bandwidth and lower access latency of 3D-stacked memory, because all of these kernels are data intensive.
Performance improvement of PIM-acc over PIM-core differes across different workloads. In some cases such as Texture Tiling, the performance improvement of PIM-Acc over PIM-Core is limited by the low computational complexity of these two kernels. But there are other cases, such as compression that benefit significantly from using PIM-Acc over PIM-Core in terms of performance, because these kernels are more compute-intensive and less data-intensive compared to texture tiling and.

## Slide 119: More on PIM for Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Lightning Talk Video (2 minutes)] [Full Talk Video (21 minutes)]

## Slide 120: Truly Distributed GPU Processing with PIM?
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
SM (Streaming Multiprocessor)

## Slide 121: Accelerating GPU Execution with PIM (I)
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 122: Accelerating GPU Execution with PIM (II)
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 123: Accelerating Linked Data Structures
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 124: Accelerating Dependent Cache Misses
Milad Hashemi, Khubaib, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "Accelerating Dependent Cache Misses with an Enhanced Memory Controller" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 125: Accelerating Runahead Execution
Milad Hashemi, Onur Mutlu, and Yale N. Patt, "Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads" Proceedings of the 49th International Symposium on Microarchitecture (MICRO), Taipei, Taiwan, October 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pdf)] [Poster (pptx) (pdf)]

## Slide 126: Two Key Questions in 3D-Stacked PIM
What are the performance and energy benefits of using 3D-stacked memory as a coarse-grained accelerator?
  By changing the entire system
  By performing simple function offloading
What is the minimal processing-in-memory support we can provide?
  With minimal changes to system and programming

## Slide 127: PEI: PIM-Enabled Instructions (Ideas)
Goal: Develop mechanisms to get the most out of near-data processing with minimal cost, minimal changes to the system, no changes to the programming model
Key Idea 1: Expose each PIM operation as a cache-coherent, virtually-addressed host processor instruction (called PEI) that operates on only a single cache block
  e.g., __pim_add(&w.next_rank, value)  pim.add r1, (r2)
  No changes sequential execution/programming model
  No changes to virtual memory
  Minimal changes to cache coherence
  No need for data mapping: Each PEI restricted to a single memory module
Key Idea 2: Dynamically decide where to execute a PEI (i.e., the host processor or PIM accelerator) based on simple locality characteristics and simple hardware predictors
  Execute each operation at the location that provides the best performance

## Slide 128: Simple PIM Operations as ISA Extensions (II)
Main Memory
w.next_rank
w.next_rank
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}
Host Processor
w.next_rank
w.next_rank
64 bytes in
64 bytes out
Conventional Architecture

## Slide 129: Simple PIM Operations as ISA Extensions (III)
Main Memory
w.next_rank
w.next_rank
Host Processor
value
8 bytes in
0 bytes out
In-Memory Addition
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pim.add r1, (r2)

## Slide 130: PEI: PIM-Enabled Instructions (Example)
Executed either in memory or in the processor: dynamic decision
  Low-cost locality monitoring for a single instruction
Cache-coherent, virtually-addressed, single cache block only
Atomic between different PEIs
Not atomic with normal instructions (use pfence for ordering)
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pfence();
pim.add r1, (r2)
pfence

## Slide 131: Example (Abstract) PEI uArchitecture
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
3D-stacked Memory
…
PCU (PEI Computation Unit)
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU (PEI
Mgmt Unit)
Example PEI uArchitecture

## Slide 132: PEI: Initial Evaluation Results
Initial evaluations with 10 emerging data-intensive workloads
  Large-scale graph processing
  In-memory data analytics
  Machine learning and data mining
  Three input sets (small, medium, large) for each workload to analyze the impact of data locality
Pin-based cycle-level x86-64 simulation
  Performance Improvement and Energy Reduction:
    47% average speedup with large input data sets
    32% speedup with small input data sets
    25% avg. energy reduction in a single node with large input data sets

## Slide 133: PEI Performance Delta: Large Data Sets
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.53918 | 0.31004 | 0.50416 | 0.45845 | 0.47598 | 0.66307 | 0.6314 | 0.44904 | 0.15358 | 0.33671 | 0.4446
Locality-Aware | 0.60067 | 0.34622 | 0.55934 | 0.51064 | 0.5286 | 0.65698 | 0.60316 | 0.44327 | 0.2149 | 0.3438 | 0.47446
(Large Inputs, Baseline: Host-Only)
47% Performance
Improvement

## Slide 134: PEI Energy Consumption
Chart: 
| Small | Medium | Large
Cache | 0.27613 | 0.22974 | 0.2138
HMC Link | 0.50415 | 0.51297 | 0.51397
DRAM | 0.21457 | 0.25453 | 0.26887
Host-side PCU | 0.0043662 | 0.0036967 | 0.0030358
Memory-side PCU | 0 | 0 | 0
PMU | 7.7323e-05 | 6.4146e-05 | 5.4225e-05
계열 7 | 0.29322 | 0.18897 | 0.14107
계열 8 | 0.68428 | 0.4834 | 0.36147
계열 9 | 0.46391 | 0.35056 | 0.26204
계열 10 | 0 | 0 | 0
계열 11 | 0.015795 | 0.011518 | 0.0085371
계열 12 | 0.0053637 | 0.0036921 | 0.0027686
Host-Only
PIM-Only
Locality-Aware
25% Energy
Reduction

## Slide 135: Simpler PIM: PIM-Enabled Instructions
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 136: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 137: Barriers to Adoption of PIM
1. Functionality of and applications & software for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System support: coherence & virtual memory
4. Runtime and compilation systems for adaptive scheduling, data mapping, access/sharing control
5. Infrastructures to assess benefits and feasibility
All can be solved with change of mindset

## Slide 138: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 139: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "Processing Data Where It Makes Sense: Enabling In-Memory Computation" Invited paper in Microprocessors and Microsystems (MICPRO), June 2019. [arXiv version]
https://arxiv.org/pdf/1903.03988.pdf

## Slide 140: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 141: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 142: Key Challenge 1: Code Mapping
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
?
Main GPU
3D-stacked memory
(memory stack)
Challenge 1: Which operations should be executed in memory vs. in CPU?
?
SM (Streaming Multiprocessor)

## Slide 143: Key Challenge 2: Data Mapping
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
Challenge 2: How should data be mapped to different 3D memory stacks?
SM (Streaming Multiprocessor)

## Slide 144: How to Do the Code and Data Mapping?
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 145: How to Schedule Code? (I)
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 146: How to Schedule Code? (II)
Milad Hashemi, Khubaib, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "Accelerating Dependent Cache Misses with an Enhanced Memory Controller" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 147: How to Schedule Code? (III)
Milad Hashemi, Onur Mutlu, and Yale N. Patt, "Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads" Proceedings of the 49th International Symposium on Microarchitecture (MICRO), Taipei, Taiwan, October 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pdf)] [Poster (pptx) (pdf)]

## Slide 148: How to Maintain Coherence? (I)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 149: How to Maintain Coherence? (II)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators" Proceedings of the 46th International Symposium on Computer Architecture (ISCA), Phoenix, AZ, USA, June 2019.

## Slide 150: How to Support Virtual Memory?
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 151: How to Design Data Structures for PIM?
Zhiyu Liu, Irina Calciu, Maurice Herlihy, and Onur Mutlu, "Concurrent Data Structures for Near-Memory Computing" Proceedings of the 29th ACM Symposium on Parallelism in Algorithms and Architectures (SPAA), Washington, DC, USA, July 2017. [Slides (pptx) (pdf)]

## Slide 152: Simulation Infrastructures for PIM
Ramulator extended for PIM
  Flexible and extensible DRAM simulator
  Can model many different memory standards and proposals
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.
  https://github.com/CMU-SAFARI/ramulator-pim
  https://github.com/CMU-SAFARI/ramulator
  [Source Code for Ramulator-PIM]

## Slide 153: Performance & Energy Models for PIM
Gagandeep Singh, Juan Gomez-Luna, Giovanni Mariani, Geraldo F. Oliveira, Stefano Corda, Sander Stujik, Onur Mutlu, and Henk Corporaal, "NAPEL: Near-Memory Computing Application Performance Prediction via Ensemble Learning" Proceedings of the 56th Design Automation Conference (DAC), Las Vegas, NV, USA, June 2019. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code for Ramulator-PIM]

## Slide 154: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 155: Concluding Remarks
It is time to design principled system architectures to solve the data handling (i.e., memory/storage) problem
Design complete systems to be truly balanced, high-performance, and energy-efficient  intelligent architectures
  Data-centric, data-driven, data-aware
Enable computation capability inside and close to memory
This can
  Lead to orders-of-magnitude improvements
  Enable new applications & computing platforms
  Enable better understanding of nature
  …
Notes: Perhaps we have taken processor-centric system design a bit too far

## Slide 156: Architectures for Intelligent Machines
Data-centric
Data-driven
Data-aware

## Slide 157
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 158: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 159: Computation in Memory An Architectural Perspective
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
20 July 2020
DAC Tutorial on Toward New Era of Compute-in-Memory

## Slide 160: Backup Slides

## Slide 161: A Bit About Myself
Onur Mutlu
  Full Professor @ ETH Zurich, since September 2015
  Strecker Professor @ Carnegie Mellon University ECE/CS, 2009-2016, 2016-…
  PhD from UT-Austin, worked at Google, VMware, Microsoft Research, Intel, AMD
  https://people.inf.ethz.ch/omutlu/
  omutlu@gmail.com (Best way to reach me)
  https://people.inf.ethz.ch/omutlu/projects.htm
Research and Teaching in:
  Computer architecture, computer systems, hardware security, bioinformatics
  Memory and storage systems
  Hardware security, safety, predictability
  Fault tolerance
  Hardware/software cooperation
  Architectures for bioinformatics, health, medicine
  …

## Slide 162: Related Overview Talks
https://www.youtube.com/onurmutlulectures
Future Computing Architectures
  https://www.youtube.com/watch?v=kgiZlSOcGFM&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=1
Enabling In-Memory Computation
  https://www.youtube.com/watch?v=njX_14584Jw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=16
Accelerating Genome Analysis
  https://www.youtube.com/watch?v=hPnSmfwu2-A&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=9
Rethinking Memory System Design
  https://www.youtube.com/watch?v=F7xZLNMIY1E&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=3
Intelligent Architectures for Intelligent Machines
  https://www.youtube.com/watch?v=n8Aj_A0WSg8&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=22

## Slide 163: Accelerated Memory Course (~6.5 hours)
ACACES 2018
  Memory Systems and Memory-Centric Computing Systems
  Taught by Onur Mutlu July 9-13, 2018
  ~6.5 hours of lectures
Website for the Course including Videos, Slides, Papers
  https://people.inf.ethz.ch/omutlu/acaces2018.html
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi-HXxomthrpDpMJm05P6J9x
All Papers are at:
  https://people.inf.ethz.ch/omutlu/projects.htm
  Final lecture notes and readings (for all topics)

## Slide 164: An Interview on Research and Education
Computing Research and Education (@ ISCA 2019)
  https://www.youtube.com/watch?v=8ffSEKZhmvo&list=PL5Q2soXY2Zi_4oP9LdL3cc8G6NIjD2Ydz
Maurice Wilkes Award Speech (10 minutes)
  https://www.youtube.com/watch?v=tcQ3zZ3JpuA&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=15

## Slide 165: Data-Centric Architectures: Properties
Process data where it resides (where it makes sense)
  Processing in and near memory structures
Low-latency & low-energy data access
  Low latency memory
  Low energy memory
Low-cost data storage & processing
  High capacity memory at low cost: hybrid memory, compression
Intelligent data management
  Intelligent controllers handling robustness, security, cost, scaling

## Slide 166: Low-Latency & Low-Energy Data Access

## Slide 167: Main Memory Latency Lags Behind
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 168: A Closer Look …
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 169: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 170: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 171: New DRAM Types Increase Latency!
Saugata Ghose, Tianshi Li, Nastaran Hajinazar, Damla Senol Cali, and Onur Mutlu, "Demystifying Workload–DRAM Interactions: An Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Phoenix, AZ, USA, June 2019. [Preliminary arXiv Version] [Abstract] [Slides (pptx) (pdf)]

## Slide 172: The Memory Latency Problem
High memory latency is a significant limiter of system performance and energy-efficiency
It is becoming increasingly so with higher memory contention in multi-core and heterogeneous architectures
  Exacerbating the bandwidth need
  Exacerbating the QoS problem
It increases processor design complexity due to the mechanisms incorporated to tolerate memory latency

## Slide 173: Retrospective: Conventional Latency Tolerance Techniques
Caching [initially by Wilkes, 1965]
  Widely used, simple, effective, but inefficient, passive
  Not all applications/phases exhibit temporal or spatial locality
Prefetching [initially in IBM 360/91, 1967]
  Works well for regular memory access patterns
  Prefetching irregular access patterns is difficult, inaccurate, and hardware-intensive
Multithreading [initially in CDC 6600, 1964]
  Works well if there are multiple threads
  Improving single thread performance using multithreading hardware is an ongoing research effort
Out-of-order execution [initially by Tomasulo, 1967]
  Tolerates cache misses that cannot be prefetched
  Requires extensive hardware resources for tolerating long latencies
None of These
Fundamentally Reduce
Memory Latency

## Slide 174: Two Major Sources of Latency Inefficiency
Modern DRAM is not designed for low latency
  Main focus is cost-per-bit (capacity)
Modern DRAM latency is determined by worst case conditions and worst case devices
  Much of memory latency is unnecessary
Our Goal: Reduce Memory Latency at the Source of the Problem

## Slide 175: Why is Memory Latency High?
DRAM latency: Delay as specified in DRAM standards
  Doesn’t reflect true DRAM device latency
Imperfect manufacturing process → latency variation
High standard latency chosen to increase yield
High
Low
DRAM Latency
DRAM A
DRAM B
DRAM C
Manufacturing Variation
Standard
Latency
Notes: To understand the latency problem, we need to go into what defines latency.
DRAM latency is the total amnt of time that the underlying hw operations need <> to retrieve data.
The DRAM standards define a single fixed time for how long these ops should take in every DRAM chip.
However, this defined delay doesn’t actually reflect the latency of the individual DRAMs.
<Timeline illustration>
Because the manufacturing process is imperfect, it introduces variation in the production chips, resulting in latency variation across different chips.
This simple illustartion shows the difference b/w the average latency across 3 different dram chips, to convey the point of latency variation.
It’s important to note that not only does latency variation exists <across> chips, but also <inside> each dram chip itself.
<Blue standard>
Since we don’t want to throw away the chips with high variation, we tolerate them.
The simple way is to <slow> down the acceptable latency so that the majority of chips can all work reliably under this high standard latency.
as we can see, the high standard latency is a result of a trade-off made for higher DRAM production yield.
---
<> Operative word

## Slide 176: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer provides multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 177: Infrastructures to Understand Such Issues
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 178: SoftMC: Open Source DRAM Infrastructure
Hasan Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 179: SoftMC
https://github.com/CMU-SAFARI/SoftMC

## Slide 180
Latency Reduction Summary of 115 DIMMs
Latency reduction for read & write (55°C)
  Read Latency: 32.7%
  Write Latency: 55.1%
Latency reduction for each timing parameter (55°C)
  Sensing: 17.3%
  Restore: 37.3% (read), 54.8% (write)
  Precharge: 35.2%
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 181
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
AL-DRAM: Real-System Performance
AL-DRAM provides high performance on
memory-intensive workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 182: Reducing Latency Also Reduces Energy
AL-DRAM reduces DRAM power consumption
Major reason: reduction in row activation time

## Slide 183: More on Adaptive-Latency DRAM
Donghyuk Lee, Yoongu Kim, Gennady Pekhimenko, Samira Khan, Vivek Seshadri, Kevin Chang, and Onur Mutlu, "Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)] [Full data sets]

## Slide 184: Tackling the Fixed Latency Mindset
Reliable operation latency is actually very heterogeneous
  Across temperatures, chips, parts of a chip, voltage levels, …
Idea: Dynamically find out and use the lowest latency one can reliably access a memory location with
  Adaptive-Latency DRAM [HPCA 2015]
  Flexible-Latency DRAM [SIGMETRICS 2016]
  Design-Induced Variation-Aware DRAM [SIGMETRICS 2017]
  Voltron [SIGMETRICS 2017]
  DRAM Latency PUF [HPCA 2018]
  DRAM Latency True Random Number Generator [HPCA 2019]
  ...
We would like to find sources of latency heterogeneity and exploit them to minimize latency (or create other benefits)

## Slide 185: Analysis of Latency Variation in DRAM Chips
Kevin Chang, Abhijith Kashyap, Hasan Hassan, Samira Khan, Kevin Hsieh, Donghyuk Lee, Saugata Ghose, Gennady Pekhimenko, Tianshi Li, and Onur Mutlu, "Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Antibes Juan-Les-Pins, France, June 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 186: Design-Induced Latency Variation in DRAM
Donghyuk Lee, Samira Khan, Lavanya Subramanian, Saugata Ghose, Rachata Ausavarungnirun, Gennady Pekhimenko, Vivek Seshadri, and Onur Mutlu, "Design-Induced Latency Variation in Modern DRAM Chips: Characterization, Analysis, and Latency Reduction Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 187: Solar-DRAM: Exploiting Spatial Variation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "Solar-DRAM: Reducing DRAM Access Latency by Exploiting the Variation in Local Bitlines" Proceedings of the 36th IEEE International Conference on Computer Design (ICCD), Orlando, FL, USA, October 2018.

## Slide 188: DRAM Latency PUFs
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 189: DRAM Latency True Random Number Generator
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019.

## Slide 190: ChargeCache: Exploiting Access Patterns
Hasan Hassan, Gennady Pekhimenko, Nandita Vijaykumar, Vivek Seshadri, Donghyuk Lee, Oguz Ergin, and Onur Mutlu, "ChargeCache: Reducing DRAM Latency by Exploiting Row Access Locality" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 191: Exploiting Subarray Level Parallelism
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, and Onur Mutlu, "A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pptx)

## Slide 192: Tiered-Latency DRAM
Donghyuk Lee, Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian, and Onur Mutlu, "Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)

## Slide 193: LISA: Low-cost Inter-linked Subarrays
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 194: The CROW Substrate for DRAM
Hasan Hassan, Minesh Patel, Jeremie S. Kim, A. Giray Yaglikci, Nandita Vijaykumar, Nika Mansourighiasi, Saugata Ghose, and Onur Mutlu, "CROW: A Low-Cost Substrate for Improving DRAM Performance, Energy Efficiency, and Reliability" Proceedings of the 46th International Symposium on Computer Architecture (ISCA), Phoenix, AZ, USA, June 2019.

## Slide 195: Reducing Refresh Latency
Anup Das, Hasan Hassan, and Onur Mutlu, "VRL-DRAM: Improving DRAM Performance via Variable Refresh Latency" Proceedings of the 55th Design Automation Conference (DAC), San Francisco, CA, USA, June 2018.

## Slide 196: Parallelizing Refreshes and Accesses
Kevin Chang, Donghyuk Lee, Zeshan Chishti, Alaa Alameldeen, Chris Wilkerson, Yoongu Kim, and Onur Mutlu, "Improving DRAM Performance by Parallelizing Refreshes with Accesses" Proceedings of the 20th International Symposium on High-Performance Computer Architecture (HPCA), Orlando, FL, February 2014. [Summary] [Slides (pptx) (pdf)]

## Slide 197: Eliminating Refreshes
Jamie Liu, Ben Jaiyen, Richard Veras, and Onur Mutlu, "RAIDR: Retention-Aware Intelligent DRAM Refresh" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pdf)

## Slide 198: Analysis of Latency-Voltage in DRAM Chips
Kevin Chang, A. Giray Yaglikci, Saugata Ghose, Aditya Agrawal, Niladrish Chatterjee, Abhijith Kashyap, Donghyuk Lee, Mike O'Connor, Hasan Hassan, and Onur Mutlu, "Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 199: VAMPIRE DRAM Power Model
Saugata Ghose, A. Giray Yaglikci, Raghav Gupta, Donghyuk Lee, Kais Kudrolli, William X. Liu, Hasan Hassan, Kevin K. Chang, Niladrish Chatterjee, Aditya Agrawal, Mike O'Connor, and Onur Mutlu, "What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Irvine, CA, USA, June 2018. [Abstract]

## Slide 200: Takeaway I
We Can Reduce
Memory Latency
with Change of Mindset

## Slide 201: Takeaway II
Main Memory Needs
Intelligent Controllers
to Reduce Latency

## Slide 202: Data-Driven and Data-Aware Architectures

## Slide 203: Corollaries: Architectures Today …
Architectures are terrible at dealing with data
  Designed to mainly store and move data vs. to compute
  They are processor-centric as opposed to data-centric
Architectures are terrible at taking advantage of vast amounts of data (and metadata) available to them
  Designed to make simple decisions, ignoring lots of data
  They make human-driven decisions vs. data-driven decisions
Architectures are terrible at knowing and exploiting different properties of application data
  Designed to treat all data as the same
  They make component-aware decisions vs. data-aware

## Slide 204: Exploiting Data to Design Intelligent Architectures

## Slide 205: System Architecture Design Today
Human-driven
  Humans design the policies (how to do things)
Many (too) simple, short-sighted policies all over the system
No automatic data-driven policy learning
(Almost) no learning: cannot take lessons from past actions
Can we design
fundamentally intelligent architectures?

## Slide 206: An Intelligent Architecture
Data-driven
  Machine learns the “best” policies (how to do things)
Sophisticated, workload-driven, changing, far-sighted policies
Automatic data-driven policy learning
All controllers are intelligent data-driven agents
How do we start?

## Slide 207: Self-Optimizing Memory Controllers

## Slide 208: Memory Controller
How to schedule requests to maximize system performance?
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 209: Why are Memory Controllers Difficult to Design?
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers, …
Need to handle DRAM refresh
Need to manage power consumption
Need to optimize performance & QoS (in the presence of constraints)
  Reordering is not simple
  Fairness and QoS needs complicates the scheduling problem
…

## Slide 210: Many Memory Timing Constraints
From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.

## Slide 211: Many Memory Timing Constraints
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 212: Memory Controller Design Is Becoming More Difficult
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
Many timing constraints for various memory types
Many goals at the same time: performance, fairness, QoS, energy efficiency, …
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories

## Slide 213: Reality and Dream
Reality: It difficult to design a policy that maximizes performance, QoS, energy-efficiency, …
  Too many things to think about
  Continuously changing workload and system behavior
Dream: Wouldn’t it be nice if the DRAM controller automatically found a good scheduling policy on its own?

## Slide 214: Self-Optimizing DRAM Controllers
Ipek+, “Self Optimizing Memory Controllers: A Reinforcement Learning Approach,” ISCA 2008.
Problem: DRAM controllers are difficult to design
  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: A memory controller that adapts its scheduling policy to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent
  It dynamically and continuously learns and employs the best scheduling policy to maximize long-term performance.

## Slide 215: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.
Goal: Learn to choose actions to maximize r0 + r1 + 2r2 + … ( 0   < 1)

## Slide 216: Self-Optimizing DRAM Controllers
Dynamically adapt the memory scheduling policy via interaction with the system at runtime
  Associate system states and actions (commands) with long term reward values: each action at a given state leads to a learned reward
  Schedule command with highest estimated long-term reward value in each state
  Continuously update reward values for <state, action> pairs based on feedback from system

## Slide 217: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 218: States, Actions, Rewards
Reward function
  +1 for scheduling Read and Write commands
  0 at all other times
  Goal is to maximize long-term data bus utilization
State attributes
  Number of reads, writes, and load misses in transaction queue
  Number of pending writes and ROB heads waiting for referenced row
  Request’s relative ROB order
Actions
  Activate
  Write
  Read - load miss
  Read - store miss
  Precharge - pending
  Precharge - preemptive
  NOP

## Slide 219: Performance Results
Large, robust performance improvements over many human-designed policies

## Slide 220: Self Optimizing DRAM Controllers
+ Continuous learning in the presence of changing environment
+ Reduced designer burden in finding a good scheduling policy. Designer specifies:
1) What system variables might be useful
2) What target to optimize, but not how to optimize it
-- How to specify different objectives? (e.g., fairness, QoS, …)
-- Hardware complexity?
-- Design mindset and flow

## Slide 221: More on Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 222: An Intelligent Architecture
Data-driven
  Machine learns the “best” policies (how to do things)
Sophisticated, workload-driven, changing, far-sighted policies
Automatic data-driven policy learning
All controllers are intelligent data-driven agents
We need to rethink design
(of all controllers)

## Slide 223: Challenge and Opportunity for Future
Self-Optimizing
(Data-Driven)
Computing Architectures

## Slide 224: Corollaries: Architectures Today …
Architectures are terrible at dealing with data
  Designed to mainly store and move data vs. to compute
  They are processor-centric as opposed to data-centric
Architectures are terrible at taking advantage of vast amounts of data (and metadata) available to them
  Designed to make simple decisions, ignoring lots of data
  They make human-driven decisions vs. data-driven decisions
Architectures are terrible at knowing and exploiting different properties of application data
  Designed to treat all data as the same
  They make component-aware decisions vs. data-aware

## Slide 225: Data-Aware Architectures
A data-aware architecture understands what it can do with and to each piece of data
It makes use of different properties of data to improve performance, efficiency and other metrics
  Compressibility
  Approximability
  Locality
  Sparsity
  Criticality for Computation X
  Access Semantics
  …

## Slide 226: One Problem: Limited Interfaces

## Slide 227: A Solution: More Expressive Interfaces

## Slide 228: Expressive (Memory) Interfaces
Nandita Vijaykumar, Abhilasha Jain, Diptesh Majumdar, Kevin Hsieh, Gennady Pekhimenko, Eiman Ebrahimi, Nastaran Hajinazar, Phillip B. Gibbons and Onur Mutlu, "A Case for Richer Cross-layer Abstractions: Bridging the Semantic Gap with Expressive Memory" Proceedings of the 45th International Symposium on Computer Architecture (ISCA), Los Angeles, CA, USA, June 2018. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video]

## Slide 229: X-MeM Aids Many Optimizations

## Slide 230: Expressive (Memory) Interfaces for GPUs
Nandita Vijaykumar, Eiman Ebrahimi, Kevin Hsieh, Phillip B. Gibbons and Onur Mutlu, "The Locality Descriptor: A Holistic Cross-Layer Abstraction to Express Data Locality in GPUs" Proceedings of the 45th International Symposium on Computer Architecture (ISCA), Los Angeles, CA, USA, June 2018. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video]

## Slide 231: An Example: Hybrid Memory Management
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
SoC
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 232: An Example: Heterogeneous-Reliability Memory
Yixin Luo, Sriram Govindan, Bikash Sharma, Mark Santaniello, Justin Meza, Aman Kansal, Jie Liu, Badriddine Khessib, Kushagra Vaid, and Onur Mutlu, "Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost via Heterogeneous-Reliability Memory" Proceedings of the 44th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Atlanta, GA, June 2014. [Summary] [Slides (pptx) (pdf)] [Coverage on ZDNet]

## Slide 233: Exploiting Memory Error Tolerance with Hybrid Memory Systems
Chart: Memory error vulnerability
| App/Data A | App/Data B | App/Data C
System/Application Crash | 1.0414 | 0.63898 | 0.24773
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory [DSN 2014]
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search workload
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 234: Another Example: EDEN for DNNs
Deep Neural Network evaluation is very DRAM-intensive (especially for large networks)
1. Some data and layers in DNNs are very tolerant to errors
2. Reduce DRAM latency and voltage on such data and layers
3. While still achieving a user-specified DNN accuracy target by making training DRAM-error-aware
Data-aware management of DRAM latency and voltage for Deep Neural Network Inference

## Slide 235
Mapping example of ResNet-50:
Example DNN Data Type to DRAM Mapping
Map more error-tolerant DNN layers
to DRAM partitions with lower voltage/latency
1
2
3
4
<2% BER
<5% BER
<6% BER
<8% BER
4 DRAM partitions with different error rates
Notes: In contrast, using a DRAM chip partitioned into four voltage domains can use a many-to-four DNN to DRAM mapping, using four different voltage values with error rates indicated by the yellow, red, green, and blue lines

## Slide 236: EDEN: Data-Aware Efficient DNN Inference
Skanda Koppula, Lois Orosa, A. Giray Yaglikci, Roknoddin Azizi, Taha Shahroodi, Konstantinos Kanellopoulos, and Onur Mutlu, "EDEN: Enabling Energy-Efficient, High-Performance Deep Neural Network Inference Using Approximate DRAM" Proceedings of the 52nd International Symposium on Microarchitecture (MICRO), Columbus, OH, USA, October 2019. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 237: Challenge and Opportunity for Future
Data-Aware
(Expressive)
Computing Architectures

## Slide 238: Recap: Corollaries: Architectures Today …
Architectures are terrible at dealing with data
  Designed to mainly store and move data vs. to compute
  They are processor-centric as opposed to data-centric
Architectures are terrible at taking advantage of vast amounts of data (and metadata) available to them
  Designed to make simple decisions, ignoring lots of data
  They make human-driven decisions vs. data-driven decisions
Architectures are terrible at knowing and exploiting different properties of application data
  Designed to treat all data as the same
  They make component-aware decisions vs. data-aware

## Slide 239: Readings, Videos, Reference Materials

## Slide 240: Some Overview Talks
https://www.youtube.com/onurmutlulectures
Future Computing Architectures
  https://www.youtube.com/watch?v=kgiZlSOcGFM&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=1
Enabling In-Memory Computation
  https://www.youtube.com/watch?v=njX_14584Jw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=16
Accelerating Genome Analysis
  https://www.youtube.com/watch?v=hPnSmfwu2-A&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=9
Rethinking Memory System Design
  https://www.youtube.com/watch?v=F7xZLNMIY1E&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=3
Intelligent Architectures for Intelligent Machines
  https://www.youtube.com/watch?v=n8Aj_A0WSg8&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=22

## Slide 241: Accelerated Memory Course (~6.5 hours)
ACACES 2018
  Memory Systems and Memory-Centric Computing Systems
  Taught by Onur Mutlu July 9-13, 2018
  ~6.5 hours of lectures
Website for the Course including Videos, Slides, Papers
  https://safari.ethz.ch/memory_systems/ACACES2018/
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi-HXxomthrpDpMJm05P6J9x
All Papers are at:
  https://people.inf.ethz.ch/omutlu/projects.htm
  Final lecture notes and readings (for all topics)

## Slide 242: Longer Memory Course (~18 hours)
Tu Wien 2019
  Memory Systems and Memory-Centric Computing Systems
  Taught by Onur Mutlu June 12-19, 2019
  ~18 hours of lectures
Website for the Course including Videos, Slides, Papers
  https://safari.ethz.ch/memory_systems/TUWien2019
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi_gntM55VoMlKlw7YrXOhbl
All Papers are at:
  https://people.inf.ethz.ch/omutlu/projects.htm
  Final lecture notes and readings (for all topics)

## Slide 243: Reference Overview Paper I
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "Processing Data Where It Makes Sense: Enabling In-Memory Computation" Invited paper in Microprocessors and Microsystems (MICPRO), June 2019. [arXiv version]
https://arxiv.org/pdf/1903.03988.pdf

## Slide 244: Reference Overview Paper II
Saugata Ghose, Kevin Hsieh, Amirali Boroumand, Rachata Ausavarungnirun, Onur Mutlu, "Enabling the Adoption of Processing-in-Memory: Challenges, Mechanisms, Future Research Directions" Invited Book Chapter, to appear in 2018. [Preliminary arxiv.org version]
https://arxiv.org/pdf/1802.00320.pdf

## Slide 245: Reference Overview Paper III
Onur Mutlu and Lavanya Subramanian, "Research Problems and Opportunities in Memory Systems" Invited Article in Supercomputing Frontiers and Innovations (SUPERFRI), 2014/2015.
https://people.inf.ethz.ch/omutlu/pub/memory-systems-research_superfri14.pdf

## Slide 246: Reference Overview Paper IV
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 247: Reference Overview Paper V
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Technical talk at MemCon 2013 (MEMCON), Santa Clara, CA, August 2013. [Slides (pptx) (pdf)] [Video] [Coverage on StorageSearch]
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 248: Reference Overview Paper VI
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 249: Reference Overview Paper VII
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version]

## Slide 250: Related Videos and Course Materials (I)
Undergraduate Digital Design & Computer Architecture Course Lecture Videos (2020, 2019, 2018, 2017, 2015, 2014, 2013)
Undergraduate Digital Design & Computer Architecture Course Materials (2020, 2019, 2018, 2015, 2014, 2013)
Graduate Computer Architecture Course Lecture Videos (2019, 2018, 2017, 2015, 2013)
Graduate Computer Architecture Course Materials (2019, 2018, 2017, 2015, 2013)
Parallel Computer Architecture Course Materials (Lecture Videos)

## Slide 251: Related Videos and Course Materials (II)
Seminar in Computer Architecture Course Lecture Videos (Spring 2020, Fall 2019, Spring 2019, 2018)
Seminar in Computer Architecture Course Materials (Spring 2020, Fall 2019, Spring 2019, 2018)
Memory Systems Course Lecture Videos (Sept 2019, July 2019, June 2019, October 2018)
Memory Systems Short Course Lecture Materials (Sept 2019, July 2019, June 2019, October 2018)
ACACES Summer School Memory Systems Course Lecture Videos (2018, 2013)
ACACES Summer School Memory Systems Course Materials (2018, 2013)

## Slide 252: Some Open Source Tools (I)
Rowhammer – Program to Induce RowHammer Errors
  https://github.com/CMU-SAFARI/rowhammer
Ramulator – Fast and Extensible DRAM Simulator
  https://github.com/CMU-SAFARI/ramulator
MemSim – Simple Memory Simulator
  https://github.com/CMU-SAFARI/memsim
NOCulator – Flexible Network-on-Chip Simulator
  https://github.com/CMU-SAFARI/NOCulator
SoftMC – FPGA-Based DRAM Testing Infrastructure
  https://github.com/CMU-SAFARI/SoftMC
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 253: Some Open Source Tools (II)
MQSim – A Fast Modern SSD Simulator
  https://github.com/CMU-SAFARI/MQSim
Mosaic – GPU Simulator Supporting Concurrent Applications
  https://github.com/CMU-SAFARI/Mosaic
IMPICA – Processing in 3D-Stacked Memory Simulator
  https://github.com/CMU-SAFARI/IMPICA
SMLA – Detailed 3D-Stacked Memory Simulator
  https://github.com/CMU-SAFARI/SMLA
HWASim – Simulator for Heterogeneous CPU-HWA Systems
  https://github.com/CMU-SAFARI/HWASim
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 254: More Open Source Tools (III)
A lot more open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 256: Referenced Papers and Talks
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en
  https://www.youtube.com/onurmutlulectures

## Slide 257: An Interview on Research and Education
Computing Research and Education (@ ISCA 2019)
  https://www.youtube.com/watch?v=8ffSEKZhmvo&list=PL5Q2soXY2Zi_4oP9LdL3cc8G6NIjD2Ydz
Maurice Wilkes Award Speech (10 minutes)
  https://www.youtube.com/watch?v=tcQ3zZ3JpuA&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=15