## Slide 1: Accelerating Genome Analysis via Algorithm-Architecture Co-Design
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
11 July 2023
DAC 2023 Special Session Talk

## Slide 2: Overview
System design for bioinformatics is a critical problem
  It has large scientific, medical, societal, personal implications
This talk is about accelerating a key step in bioinformatics: genome sequence analysis
  Especially techniques for read mapping
Many bottlenecks exist in accessing and manipulating huge amounts of genomic data during analysis
Many recent ideas to accelerate read mapping
  My personal journey since September 2006

## Slide 3: Our Dream (circa 2007)
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
  Which of these DNAs does this DNA segment match with?
  What is the likely genetic disposition of this patient to this drug?
  What disease/condition might this particular DNA/RNA piece associated with?
  . . .

## Slide 4: We Need Faster & Scalable Genome Analysis
Predicting the presence and relative abundance of microbes in a sample
Understanding genetic variations, species, evolution, …
Rapid surveillance of disease outbreaks
Developing personalized medicine
And, many, many other applications …
Notes: Knowing what organisms are present in a given environmental sample and how abundant are they

## Slide 5: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 6: A Few Overview Readings (I)
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose,
Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey”
IEEE Micro, August 2020.
https://arxiv.org/pdf/2008.00961.pdf

## Slide 7: A Few Overview Readings (II)
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]
https://arxiv.org/pdf/2106.06433.pdf

## Slide 8: A Few Overview Readings (III)
Mohammed Alser, Joel Lindegger, Can Firtina, Nour Almadhoun, Haiyu Mao, Gagandeep Singh, Juan Gomez-Luna, Onur Mutlu
“From Molecules to Genomic Variations: Intelligent Algorithms and Architectures for Intelligent Genome Analysis”
Computational and Structural Biotechnology Journal, 2022
[Source code]
https://arxiv.org/pdf/2205.07957.pdf

## Slide 9: Accelerating Genome Analysis [DAC 2023]
Onur Mutlu and Can Firtina, "Accelerating Genome Analysis via Algorithm-Architecture Co-Design" Invited Special Session Paper in Proceedings of the 60th Design Automation Conference (DAC), San Francisco, CA, USA, July 2023. [arXiv version]
https://arxiv.org/pdf/2305.00492.pdf

## Slide 10: Problems with (Genome) Analysis Today
Special-Purpose Machine
for Data Generation
General-Purpose Machine
for Data Analysis
FAST SLOW
Slow and inefficient processing capability
This picture is similar for many “data generators & analyzers” today
Large amounts of data movement

## Slide 11: Algorithm-Arch-Device Co-Design is Critical
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (expanded view)

## Slide 12: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 13: DNA Under Electron Microscope
human chromosome #12
from HeLa’s cell
Notes: Henrietta Lacks,

## Slide 14
CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCC
GGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTG

## Slide 15: DNA Sequencing
Goal:
  Find the complete sequence of A, C, G, T’s in an organism’s DNA
Challenge:
  There is no machine that takes long DNA as an input, and gives the complete sequence as output
  All sequencing machines chop DNA into pieces and identify relatively small pieces (but not how they fit together)

## Slide 16
Genome Sequencers
… and more! All produce data with different properties.
Roche/454
Illumina HiSeq2000
Ion Torrent PGM
Ion Torrent Proton
AB SOLiD
Oxford Nanopore GridION
Oxford Nanopore MinION
Complete
Genomics
Illumina MiSeq
Pacific Biosciences RS
Illumina
NovaSeq
6000

## Slide 17: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION

## Slide 18: Newer Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version] [Slides (pptx) (pdf)] [Talk Video at AACBB 2019]
Oxford Nanopore MinION

## Slide 19: Types of Genomic Reads
Wenger+, "Accurate circular consensus long-read sequencing improves variant detection and assembly of a human genome", Nature Biotechnology, 2019
But still very expensive!
https://labs.wsu.edu/genomicscore/illumina-sequencing/
https://pacbio.gs.washington.edu/
Long: 10-20 kb
Accurate: 99.8%
Notes: By sequencing the same DNA segment many times (10 to 30 times), we can have accurate more longer reads.

## Slide 20: Genome Sequencing
Large DNA molecule
Small DNA fragments
Reads
ACGTACCCCGT
GATACACTGTG
TTTTTTTAATT
CTAGGGACCTT
ACGACGTAGCT
AAAAAAAAAA
ACGAGCGGGT
Notes: As the whole genome of most organisms cannot be sequenced all at once, the genome is broken into smaller fragments.
After each fragment is sequenced, small pieces of DNA sequences (i.e. reads) are generated.

## Slide 21: One Problem
Need to construct
the entire genome
from many sequenced reads

## Slide 22: Read Mapping
Map many short DNA fragments (reads) to a known reference genome with some differences allowed
Reference genome
Reads
DNA, logically
DNA, physically
Mapping short reads to reference genome is challenging (billions of 50-300 base pair reads)
Notes: Read mapping is a post processing procedure after DNA sequencing. It maps the data output from a DNA sequencer, which are many short DNA fragments, to a known reference genome, with some minor differences allowed.
To illustrate the problem better, let us take a closer look at the DNA itself. Logically, the DNA is a double stranded long string. In reality, within a cell they folded into a sphere in the nucleus like a ball of wool. Since it is very hard to disentangle the DNA at molecular level, to extract the information out, a sequencer cuts the mass into many short DNA pieces which are called reads.
A mapper’s job is to find where these DNA short reads are most likely to be originally placed so that later we can assemble them in the correct order to restore the original DNA.
Mapping these short reads, up to billions of them, with each one being 50 to 300 base-pairs long, to the reference genome is challenging.

## Slide 23: Read Mapping for Metagenomic Analysis
Reference Database
Reads in
“text format”
Genetic material recovered directly from environmental samples
Reads from different unknown donors at sequencing time are mapped to many known reference genomes
Notes: Read mapping is a post processing procedure after DNA sequencing. It maps the data output from a DNA sequencer, which are many short DNA fragments, to a known reference genome, with some minor differences allowed.
To illustrate the problem better, let us take a closer look at the DNA itself. Logically, the DNA is a double stranded long string. In reality, within a cell they folded into a sphere in the nucleus like a ball of wool. Since it is very hard to disentangle the DNA at molecular level, to extract the information out, a sequencer cuts the mass into many short DNA pieces which are called reads.
A mapper’s job is to find where these DNA short reads are most likely to be originally placed so that later we can assemble them in the correct order to restore the original DNA.
Mapping these short reads, up to billions of them, with each one being 50 to 300 base-pairs long, to the reference genome is challenging.

## Slide 24: Matching Each Read to Reference Genome
Reference Genome .FASTA file:
Sequenced Reads .FASTQ file:

## Slide 25: Base-by-Base Comparison
Notes: (f) Once the pre-alignment filter accepts the alignment between a read and a region in the reference genome then DP-based (or non-DP based) verification algorithms are used to generate the alignment file (in BAM or SAM formats), which contains alignment information such as the exact number of differences, location of each difference, and their type.

## Slide 26: Read Alignment/Verification
Edit distance is defined as the minimum number of edits (i.e., insertions, deletions, or substitutions) needed to make the read exactly match (i.e., align with) the reference segment
N | E | - | T | H | E | R | L | A | N | D | S
S | W | I | T | Z | E | R | L | A | N | D | -
NETHERLANDS x SWITZERLAND
match
deletion
insertion
mismatch
Notes: http://www.let.rug.nl/kleiweg/lev/

## Slide 27: Challenges in Read Mapping
Need to find many mappings of each read
  A short read may map to many locations, especially with High-Throughput DNA Sequencing technologies
  How can we find all mappings efficiently?
Need to tolerate small variances/errors in each read
  Each individual is different: Subject’s DNA may slightly differ from the reference (Mismatches, insertions, deletions) + Sequencer errors
  How can we efficiently map each read with up to e errors present?
Need to map each read very fast (i.e., performance is important)
  Human DNA is 3.2 billion base pairs long  Millions to billions of reads (State-of-the-art mappers take weeks to map a human’s DNA)
  How can we design a much higher performance read mapper?
Notes: There are three main challenges.
First. The mapper needs to find many mappings for each read. Because the read is so short, they can map to multiple locations in the reference genome. How can we efficiently find all mappings of a read?
Second. The mapper needs to tolerate small variance or errors in each read. Since individuals are different, the subject’s DNA might slightly differs from the reference DNA, which can be mismatches, insertions or deletions of base pairs. How can we efficiently map each read with up to a number of e errors present?
Third. The mapper needs to map each read very fast. In another word, performance is important. Because the human DNA is 3.2 billion base-pairs long and each read is only hundreds of base-pairs long, there can be billions of reads subjected to mapping for an individual human. Current state of the art mappers take weeks to map a human’s DNA. So the question is, how can we design a much higher performance read mapper?

## Slide 28: Why Is Read Alignment Slow?
Quadratic-time dynamic-programming algorithm(s)
etc
etc
Data dependencies limit the computation parallelism
Entire matrix computed even though strings may be dissimilar
etc
Notes: 1- Read alignment follows the basic dynamic-programming doctrine which runs in a quadratic time.
2- Data dependencies between the entries limits the parallelism. Each cell depends or three pre-computed cells (immediate left, upper, and upper-left cells). Thus, we can compute the vectors one after another but not in parallel. Left-to-right, or top-to-bottom, anti-diagonal.
3- We can solve a significant amount of time, If we can find a way to detect the incorrect mappings with cheap heuristics, much cheaper than computing the alignment.

## Slide 29: Computational Cost is Mathematically Proven
https://arxiv.org/abs/1412.0348

## Slide 30: Read Mapping Techniques in 111 Pages
Mohammed Alser, Jeremy Rotman, Dhrithi Deshpande, Kodi Taraszka, Huwenbo Shi, Pelin Icer Baykal, Harry Taegyun Yang, Victor Xue, Sergey Knyazev, Benjamin D. Singer, Brunilda Balliu, David Koslicki, Pavel Skums, Alex Zelikovsky,
Can Alkan, Onur Mutlu, Serghei Mangul
"Technology dictates algorithms: Recent developments in read alignment"
Genome Biology, 2021
[Source code]
In-depth analysis of 107 read mappers (1988-2020)

## Slide 31
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 32
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
300 M
bases/min
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Illumina HiSeq4000
2 M
bases/min
on average
(0.6%)
We Are Bottlenecked in Read Mapping
Notes: Typical sequencer machine generates a flood of reads, for example, Illumina HiSeq4000 generates 300 million bases/minute.
However, existing computer alignment algorithms can only process 0.6% of these reads in the same amount of time.
This gap is widening as more advanced sequencers are made available in the market.

## Slide 33: The Read Mapping Bottleneck
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Read Sequencing
Read Mapping
* BWA-MEM
** HiSeqX10, MinION
*
**
150x slower
Million
bases/minute
300
Million
bases/minute
2
Notes: 12.48
5.2 CPU hours
144x
60 CPU hours
BWA-MEM
25 minutes
Illumine HiSeq X10
25 minutes
Nanopore MinION
Short reads generated in a day using today’s HTS machines (e.g., Illumine HiSeq X10) can be mapped to the human reference genome using BWA-MEM [36], a popular and widely-used read mapper, in 12.5 CPU (central processing unit) days when running on a single core [66, 67]. BWA-MEM also takes about 2.5 CPU days to map long reads that are generated in 25 minutes using today’s Nanopore MinION sequencer [68]

## Slide 34: The Read Mapping Bottleneck
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Human whole
genomes
Human
1
Illumina NovaSeq 6000
48
at 30× coverage
in about 2 days
genome
32 CPU hours
on a 48-core processor
Chart: 
| Read Mapping | Others
Sales | 0.71 | 0.29
Goyal+, "Ultra-fast next generation human genome sequencing data processing using DRAGENTM bio-IT processor for precision medicine”, Open Journal of Genetics, 2017.
Notes: 12.48
5.2 CPU hours
144x
60 CPU hours
BWA-MEM
25 minutes
Illumine HiSeq X10
25 minutes
Nanopore MinION
Short reads generated in a day using today’s HTS machines (e.g., Illumine HiSeq X10) can be mapped to the human reference genome using BWA-MEM [36], a popular and widely-used read mapper, in 12.5 CPU (central processing unit) days when running on a single core [66, 67]. BWA-MEM also takes about 2.5 CPU days to map long reads that are generated in 25 minutes using today’s Nanopore MinION sequencer [68]

## Slide 35: Problems with (Genome) Analysis Today
Special-Purpose Machine
for Data Generation
General-Purpose Machine
for Data Analysis
FAST SLOW
Slow and inefficient processing capability
This picture is similar for many “data generators & analyzers” today
Large amounts of data movement

## Slide 36: Accelerating Read Mapping
Alser+, “Accelerating Genome Analysis: A Primer on an Ongoing Journey”, IEEE Micro, 2020.

## Slide 37: Detailed Analysis of Tackling the Bottleneck
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose,
Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey”
IEEE Micro, August 2020.

## Slide 38: Genomics Course (Fall 2022)
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=bioinformatics
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=bioinformatics
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=nA41964-9r8&list=PL5Q2soXY2Zi8tFlQvdxOdizD_EhVAMVQV
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=DEL_5A_Y3TI&list=PL5Q2soXY2Zi8NrPDgOR1yRU_Cxxjw-u18
Project course
  Taken by Bachelor’s/Master’s students
  Genomics lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 39: BIO-Arch Workshop at RECOMB 2023
April 14, 2023
https://safari.ethz.ch/recomb23-arch-workshop/
https://www.youtube.com/watch?v=2rCsb4-nLmg

## Slide 40: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 41: Read Mapping Execution Time (Modern)
ONT FASTQ size: 103MB (151 reads), Mean length: 356,403 bp, std: 173,168 bp, longest length: 817,917 bp
Chart: 
| KSW2 | Seed Chaining | Sorting Seeds | Collect Matching Seeds | Collect Minimizers
Sales | 0.46 | 0.16 | 0.29 | 0.08 | 0.02
>60%
of the read mapper’s execution time is spent in sequence alignment
minimap2

## Slide 42: Overarching Key Idea
Filter fast before you align
Minimize costly
edit distance computations
(“approximate string comparisons”)

## Slide 43: Overarching Key Idea
Sequenced Reads
Similar to Reference
Too Dissimilar to Reference
Focus processing power
on these
(e.g., edit distance comp.)
Quickly find these
and filter them out
w/o costly computation

## Slide 44: Our First Filter: Pure Software Approach
Download the source code and try for yourself
  Download link to FastHASH
Xin+, "Accelerating Read Mapping with FastHASH", BMC Genomics 2013.

## Slide 45: Shifted Hamming Distance: SIMD Acceleration
Xin+, "Shifted Hamming Distance: A Fast and Accurate SIMD-friendly Filter
to Accelerate Alignment Verification in Read Mapping”, Bioinformatics 2015.
https://github.com/CMU-SAFARI/Shifted-Hamming-Distance

## Slide 46: Hamming Distance ()
I
S
T
A
N
B
U
L
I
S
T
A
N
B
U
L
8 matches 0 mismatches
3 matches 5 mismatches
To cancel the effect of a deletion, we need to shift in the right direction
Edit = 1 Deletion
Notes: Our second proposed method to accelerate read mappers is to parallelize the matrix computation.
To explain our new matrix, here is an example of exact match sequences. Now imagine there is a base deletion for any reason.

## Slide 47: Insight: Shifting a String Helps Similarity Search
I
S
T
A
N
B
U
L
I
S
T
N
B
U
L
3 matches 5 mismatches
To cancel the effect of the deletion, we need to shift in the right direction
Notes: After deletion, the trailing bases will be shifted to left to form a single sequence.
But when we align it back, we get too many mismatches though the number of edits is only ONE.
To cancel the effect of deletion and correctly align the sequences, we have to shift the sequence to right and align again.

## Slide 48: Insight: Shifting a String Helps Similarity Search
I
S
T
A
N
B
U
L
I
S
T
N
B
U
L
7 matches 1 mismatch
I
S
T
N
B
U
L
Notes: With the help of another right-shifted copy of the original sequence, we can have more similarities between the two sequences. Think about other scenarios where you have an insertion? Or a combination of deletion and insertion?

## Slide 49: Shifted Hamming Distance
I
S
T
N
B
U
L
7 matches 1 mismatch
XOR
XOR
AND
Edit = 1 Deletion
I
S
T
N
B
U
L
0
0
0
1
1
1
1
0
0
0
0
1
1
1
0 0 0 1 0 0 0 0
Count 1’s
I
S
T
A
N
B
U
L
Notes: With the help of another right-shifted copy of the original sequence, we can have more similarities between the two sequences. Think about other scenarios where you have an insertion? Or a combination of deletion and insertion?

## Slide 50: Highly Parallel Matrix Computation
We need to compute 2E+1 vectors, E=edit distance threshold
dp[i][j]= 0 if X[i]=Y[j]
1 if X[i]≠Y[j]
No data dependencies!
2 Deletion Hamming masks
2 Insertion Hamming masks
Reference
Query
Notes: So this is how we compute the filter matrix. We pairwise compare each character from a sequence to its corresponding character from the other sequence. Match =0, Mismatch=1
The yellow diagonal vector represents XOR between the two sequences. The pink diagonal vectors represent right-shifted copies of the query sequence then compared to the reference. The blue vectors represent left-shifted copies of the query. By this we can guarantee that we can correctly examine any two sequences regardless the type of edits they have. AND NO DATA DEPENDENCIES between the cells.

## Slide 51: GateKeeper: FPGA-Based Alignment Filtering
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 52: GateKeeper Accelerator Architecture
Maximum data throughput =~13.3 billion bases/sec
Can examine 8 (300 bp) or 16 (100 bp) mappings concurrently at 250 MHz
Occupies 50% (100 bp) to 91% (300 bp) of the FPGA slice LUTs and registers
Notes: Here, we present the architecture of GateKeeper. Each processing core is able to examine a single mapping in a single clock cycle. We integrate many hardware processing cores in the architecture of GateKeeper for examining many mappings in a parallel fashion. The input read-reference pairs are transferred from the host to the FPGA via PCIe third generation 4-lane at the rate of 13.3 billion bases/sec. With this data throughput, we can have 16 processing cores work concurrently to examine 16 read-reference pairs. Our architecture occupies only 50% of the FPGA resource for a read length of 100 bp and 91% for a read length of 300 bp.

## Slide 53: FPGA Chip Layout
Read length:
300 bp
Error threshold:
E=15

## Slide 54: GateKeeper: Speed & Accuracy Results
90x-130x faster filter
than SHD (Xin et al., 2015) and the Adjacency Filter (Xin et al., 2013)
4x lower false accept rate
than the Adjacency Filter (Xin et al., 2013)
10x speedup in read mapping
with the addition of GateKeeper to the mrFAST mapper (Alkan et al., 2009)
Freely available online github.com/BilkentCompGen/GateKeeper

## Slide 55: GateKeeper Conclusions
FPGA-based pre-alignment greatly speeds up read mapping
  10x speedup of a state-of-the-art mapper (mrFAST)
FPGA-based pre-alignment can be integrated with the sequencer
  It can help to hide the complexity and details of the FPGA
  Enables real-time filtering while sequencing
  Paves the way to on-device genome analysis

## Slide 56: More on GateKeeper
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 57: Algorithm-Arch-Device Co-Design is Critical
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (expanded view)

## Slide 58: Shouji (障子) [Alser+, Bioinformatics 2019]
Mohammed Alser, Hasan Hassan, Akash Kumar, Onur Mutlu, and Can Alkan, "Shouji: A Fast and Efficient Pre-Alignment Filter for Sequence Alignment" Bioinformatics, [published online, March 28], 2019. [Source Code] [Online link at Bioinformatics Journal]

## Slide 59: Hardware Implementation
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Counting is performed concurrently for all bit-vectors and
all sliding windows in a single clock cycle using multiple 4-input LUTs

## Slide 60: SneakySnake [Alser+, Bioinformatics 2020]
Mohammed Alser, Taha Shahroodi, Juan-Gomez Luna, Can Alkan, and Onur Mutlu, "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs" Bioinformatics, to appear in 2020. [Source Code] [Online link at Bioinformatics Journal]

## Slide 61: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches
Dot plot, dot matrix
(Lipman and Pearson, 1985)

## Slide 62: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches
Key idea:
  Reduce the approximate string matching problem to the Single Net Routing problem in VLSI chip layout
VLSI chip layout

## Slide 63: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches
Key idea:
  Reduce the approximate string matching problem to the Single Net Routing problem in VLSI chip layout
Key result:
  SneakySnake is up to four orders of magnitude more accurate than Shouji (Bioinformatics’19) and GateKeeper (Bioinformatics’17)
  SneakySnake greatly accelerates state-of-the-art CPU sequence aligners, Edlib (Bioinformatics’17) and Parasail (BMC Bioinformatics’16)
    by up to 37.7× and 43.9× (>12× on average), on CPUs
    by up to 413× and 689× (>400× on average) with FPGAs/GPUs

## Slide 64: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
E = 3
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 65: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
E = 3
ENTRANCE
EXIT
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 66: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Optimal Routing Path
Examining the Snake Survival
3
EXIT
2
1
0
0
0
4
0
2
0
0
ENTRANCE
0
0
0
4
1
0
1
0
1
1
0
1
0
0
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 67: SneakySnake Walkthrough
Building Neighborhood Map
Finding the Routing Travel Path
Examining the Snake Survival
This is what you actually need to build and it can be done on-the-fly!
ENTRANCE
EXIT
3
Notes: After computing the binary matrix of GateKeeper, we need to backtrack all matches (consecutive zeros highlighted in green) between the two sequences. In GateKeeper, we AND all diagonal bit-vectors of the matrix together and produce a single bit-vector that represents the largest possible number of matches between the two sequences. Due to the use of AND operation, we need to ignore the meaningless short zeros (one or two zeros). Final step is to count the number of zeros in the AND mask and if exceeds the threshold then the filter passes the two sequences.

## Slide 68: FPGA Resource Analysis
FPGA resource usage for a single filtering unit of GateKeeper, Shouji, and Snake-on-Chip for a sequence length of 100 and under different edit distance thresholds (E).

## Slide 69: Key Results of SneakySnake
  SneakySnake is up to four orders of magnitude more accurate than Shouji (Bioinformatics’19) and GateKeeper (Bioinformatics’17)
  Short reads:
    SneakySnake accelerates Edlib (Bioinformatics’17) and Parasail (BMC Bioinformatics’16) by
    up to 37.7× and 43.9× (>12× on average), on CPUs
    up to 413× and 689× (>400× on average) using FPGAs/GPUs
  Long reads:
    SneakySnake accelerates Parasail and KSW2 by 140.1× and 17.1× on average, respectively, on CPUs

## Slide 70: More on SneakySnake [Alser+, Bioinformatics 2020]
Mohammed Alser, Taha Shahroodi, Juan-Gomez Luna, Can Alkan, and Onur Mutlu, "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs" Bioinformatics, to appear in 2020. [Source Code] [Online link at Bioinformatics Journal]

## Slide 71: GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 72: GenASM: ASM Framework for GSA
GenASM: First ASM acceleration framework for GSA
  Based on the Bitap algorithm
    Uses fast and simple bitwise operations to perform ASM
  Modified and extended ASM algorithm
    Highly-parallel Bitap with long read support
    Bitvector-based novel algorithm to perform traceback
  Co-design of our modified scalable and memory-efficient algorithms with low-power and area-efficient hardware accelerators
Our Goal:
Accelerate approximate string matching
by designing a fast and flexible framework,
which can accelerate multiple steps of genome sequence analysis
Notes: [CLICK] Our goal in this work is to design a fast and flexible framework for both short and long reads, which can accelerate multiple steps of genome sequence analysis (GSA).
[CLICK] To this end, we propose GenASM
[CLICK] We base GenASM on Bitap, an ASM algorithm that uses only fast and simple bitwise operations, making it amenable to efficient hardware acceleration. To our knowledge, GenASM is the first work that enhances and accelerates Bitap, and also it is the first ASM acceleration framework for genome sequence analysis.
[CLICK] We modify Bitap to support long reads and to enable parallelization.
We also develop a novel Bitap-compatible algorithm for traceback, which uses information collected during ASM about the different types of errors to identify the optimal alignment of reads.
[CLICK] And, we co-design specialized, low-power and area-efficient hardware for both algorithms.

## Slide 73: GenASM: Hardware Design
GenASM-DC
GenASM-TB
GenASM-DC:
generates bitvectors
and performs edit
Distance Calculation
GenASM-TB: performs TraceBack and assembles the optimal alignment
Host CPU
TB-SRAM1
TB-SRAM2
TB-SRAMn
GenASM-TB
Accelerator
GenASM-DC
Accelerator
GenASM-TB
Accelerator
GenASM-DC
Accelerator
Main Memory
DC-SRAM
DC-SRAM
GenASM-DC
GenASM-TB
TB-SRAM1
TB-SRAM2
TB-SRAMn
.
.
.
Notes: Our co-designed hardware consists of two components:
(1) GenASM-DC, which provides hardware support to efficiently execute our modified Bitap algorithm to perform distance calculation; and
(2) GenASM-TB, which provides hardware support to efficiently execute our novel traceback algorithm to find the optimal alignment.
GenASM also has two types of SRAM buffers:
DC-SRAM, and
TB-SRAMs

## Slide 74: GenASM-DC: Hardware Design
Linear cyclic systolic array based accelerator
  Designed to maximize parallelism and minimize memory bandwidth and memory footprint
Processing Block (PB)
Processing Core (PC)
Notes: [CLICK] We implement GenASM-DC as a linear cyclic systolic array based accelerator, using small and very simple logic components.
[CLICK] This design helps us to maximize parallelism and minimize memory BW and footprint.
[CLICK] Processing Core is the basic compute component which computes the intermediate bitvectors
[CLICK] and when we add the flip-flop-based storage logic around Processing Core, we define a Processing Element (PE)
[CLICK] Multiple PEs are concatenated to define a Processing Block
[CLICK] We also have DC-SRAM, which stores the reference text, the pattern bitmasks for the query read, and the intermediate data generated from PEs, and we also have
[CLICK] TB-SRAMs, which store the intermediate bitvectors generated by each PE of GenASM-DC for later use by GenASM-TB.

## Slide 75: GenASM-TB: Hardware Design
Bitwise Comparisons
CIGAR string
Last CIGAR
<<
match
CIGAR
out
1
2
.
.
64
192
insertion
deletion
subs
64
64
64
64
1
2
Next Rd Addr Compute
3
GenASM-TB
Very simple logic:
  ❶Reads the bitvectors from one of the TB-SRAMs using the computed address
  ❷Performs the required bitwise comparisons to find the traceback output for the current position
  ❸Computes the next TB-SRAM address to read the new set of bitvectors
Bitwise Comparisons
CIGAR string
Last CIGAR
<<
match
CIGAR
out
1
2
.
.
64
192
insertion
deletion
subs
64
64
64
64
to main
memory
1
2
Next Rd Addr Compute
3
1.5KB
TB-SRAM1
1.5KB
TB-SRAM2
1.5KB
TB-SRAM64
1
2
3
Notes: [CLICK] We implement GenASM-TB hardware using very simple logic, which
[CLICK] 1) reads the bitvectors from one of the TB-SRAMs using the computed address,
[CLICK] 2) performs the required bitwise comparisons to find the traceback output for the current position, and
[CLICK] 3) computes the next TB-SRAM address to read the new set of bitvectors.
After GenASM-TB finds the complete traceback output, [CLICK] it writes this output to main memory and completes its execution.

## Slide 76: Key Results – Area and Power
Based on our synthesis of GenASM-DC and GenASM-TB accelerator datapaths using the Synopsys Design Compiler with a 28nm LP process:
  Both GenASM-DC and GenASM-TB operate @ 1GHz
  Total (1 vault): 0.334 mm2 0.101 W
  Total (32 vaults): 10.69 mm2 3.23 W
  % of a Xeon CPU core: 1% 1%
Notes: [CLICK] We synthesize our DC and TB accelerator datapaths with a typical 28nm low-power process:
[CLICK] Both accelerators operates at 1GHz.
[CLICK] We find that for 32 GenASM accelerator (one for each HMC vault), total area overhead is ten point sixty nine millimeter square and total power consumption is three point twenty-three watts.
We observe that both area and power consumption of GenASM (at 1 vault) is around 1% of the area and power consumption of a single Xeon CPU core.

## Slide 77: Key Results – Area and Power
Based on our synthesis of GenASM-DC and GenASM-TB accelerator datapaths using the Synopsys Design Compiler with a 28nm LP process:
  Both GenASM-DC and GenASM-TB operate @ 1GHz
  GenASM has low area and power overheads
Notes: Thus, GenASM has low area and power overheads.

## Slide 78: Use Cases of GenASM
Indexing
Seeding
Pre-Alignment Filtering
Read Alignment
Reference genome
Hash table based index
Candidate mapping locations
Optimal alignment
Reads from sequenced genome
Remaining candidate mapping locations
Indexing
Seeding
Notes: GenASM is flexible and can be used for a number of use cases.
In this work, we evaluate three of them in detail and two of them are from the read mapping pipeline:
Pre-alignment filtering and read alignment

## Slide 79: Use Cases of GenASM (cont’d.)
Read Alignment Step of Read Mapping
  Find the optimal alignment of how reads map to candidate reference regions
Pre-Alignment Filtering for Short Reads
  Quickly identify and filter out the unlikely candidate reference regions for each read
Edit Distance Calculation
  Measure the similarity or distance between two sequences
We also discuss other possible use cases of GenASM in our paper:
  Read-to-read overlap finding, hash-table based indexing, whole genome alignment, generic text search
Notes: [CLICK] (1) read alignment
is the most time consuming step of read mapping that we align each read to all of its candidate reference regions and then find the optimal alignment.
[CLICK] (2) in pre-alignment filtering for short reads,
we aim to quickly identify and filter out the unlikely candidate reference regions of each read by approximating the edit distance between them and filter out if it is above a threshold.
[CLICK] And our third use case is edit distance calculation
Which is one of the fundamental operations in genomics that measures the similarity or distance btw two sequences
In our paper, we also briefly discuss several other use cases such as generic text search

## Slide 80: Key Results
Read Alignment
116× speedup, 37× less power than Minimap2 (state-of-the-art SW)
111× speedup, 33× less power than BWA-MEM (state-of-the-art SW)
3.9× better throughput, 2.7× less power than Darwin (state-of-the-art HW)
1.9× better throughput, 82% less logic power than GenAx (state-of-the-art HW)
Pre-Alignment Filtering
3.7× speedup, 1.7× less power than Shouji (state-of-the-art HW)
Edit Distance Calculation
22–12501× speedup, 548–582× less power than Edlib (state-of-the-art SW)
9.3–400× speedup, 67× less power than ASAP (state-of-the-art HW)
Notes: We find that, for all the three use cases, GenASM is significantly more efficient in terms of both speed and power consumption than state-of-the-art software and hardware baselines

## Slide 81: More on GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 82: Scrooge: Faster Approximate String Matching
Joël Lindegger, Damla Senol Cali, Mohammed Alser, Juan Gómez-Luna, Nika Mansouri Ghiasi, and Onur Mutlu, "Scrooge: A Fast and Memory-Frugal Genomic Sequence Aligner for CPUs, GPUs, and ASICs" Bioinformatics, [published online on] 24 March 2023. [Online link at Bioinformatics Journal] [arXiv preprint] [Scrooge Source Code]
https://arxiv.org/pdf/2208.09985.pdf
https://github.com/cmu-safari/scrooge

## Slide 83: Our Goals
Compete with state-of-the-art pairwise sequence aligners like Edlib, KSW2, and BiWFA
Build a practical and efficient implementation of the GenASM algorithm for multiple computing platforms

## Slide 84: Scrooge
Three novel algorithmic improvements which address inefficiencies in the GenASM algorithm
Efficient open-source implementations for CPUs and GPUs
Key Results
Scrooge consistently outperforms GenASM
2.1x speedup over GenASM on CPU
5.9x speedup over GenASM on GPU
3.6x better area efficiency and 3.6x less power than GenASM as an ASIC
Scrooge consistently outperforms state-of-the-art CPU and GPU baselines, including KSW2, Edlib, and BiWFA

## Slide 85: Scrooge on GitHub
Scrooge on GitHub

## Slide 86: Scrooge Talk Video
https://www.youtube.com/watch?v=2rCsb4-nLmg&t=20313s

## Slide 87: Accelerating Sequence-to-Graph Mapping
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 88: Genome Sequence Analysis
Sequence-to-Sequence (S2S) Mapping
Sequence-to-Graph (S2G) Mapping
Sequence-to-graph mapping results in notable quality improvements.
However, it is a more difficult computational problem,
with no prior hardware design.
Mapping the reads to a reference genome (i.e., read mapping) is a critical step in genome sequence analysis
Linear Reference: ACGTACGT
Read: ACGG
Alternative Sequence: ACGGACGT
Alternative Sequence: ACGTTACGT
Alternative Sequence: ACG‒ACGT
Graph-based Reference:
Read: ACGG
Notes: Read mapping, which is the process of mapping the reads to a reference genome is a critical step in genome sequence analysis
Traditionally, we perform seq2seq mapping, where we
Map reads collected from an individual to a known linear reference genome sequence
Emphasizes the genetic variations that are present in the single reference genome
Ignores other variations that are not represented in the single linear reference sequence
Introduces reference bias
However, s2s mapping is a well studied problem with many available tools and accelerators
Recent works replace the linear reference sequence with a graph-based representation of the reference genome (genome graph). Thus, we can perform seq2graph mapping.
Captures the genetic variations and diversity across many individuals in a population
[CLICK] Results in notable quality improvements in GSA

## Slide 89: SeGraM: First Graph Mapping Accelerator
SeGraM: First universal algorithm/hardware co-designed genomic mapping accelerator that can effectively and efficiently support:
Sequence-to-graph mapping
Sequence-to-sequence mapping
Both short and long reads
Our Goal:
Specialized, high-performance, scalable, and low-cost algorithm/hardware co-design that alleviates bottlenecks in multiple steps of sequence-to-graph mapping
Notes: [CLICK] Thus, our goal is to come up with a specialized, high-performance, scalable, and low-cost algorithm/hardware co-design that alleviates bottlenecks in both the seeding and alignment steps of sequence-to-graph mapping.
[CLICK] To this end, we propose SeGraM, a universal algorithm/hardware co-designed genomic mapping accelerator that can effectively and efficiently support both sequence-to-graph mapping and sequence-to-sequence mapping, for both short and long reads. To our knowledge, SeGraM is the first algorithm/hardware co-design for accelerating
sequence-to-graph mapping.

## Slide 90: Sequence-to-Graph Mapping Pipeline
Pre-Processing
Steps (Offline)
Seed-and-Extend
Steps (Online)
Indexing
(index the nodes of the graph)
Seeding
(query the index & find the seed matches)
Filtering/Chaining/Clustering
(filter out dissimilar query read and subgraph pairs)
S2G Alignment
(perform distance/score calculation & traceback)
Linear reference genome
Known genetic variations
Reads from sequenced
genome
0.2
1
2
3
Genome Graph Construction
(construct the graph using a linear reference genome and variations)
0.1
Genome graph
Hash-table-based index (of graph nodes)
Candidate mapping locations (subgraphs)
Remaining candidate mapping locations (subgraphs)
Optimal alignment between read & subgraph
Notes: Which brings us to seq2graph mapping.
Sequence-to-graph mapping pipeline has [CLICK] two pre-processing and [CLICK] three main steps.
[CLICK] The first pre-processing step constructs the genome graph using a linear reference genome and the associated variations for that genome.
[CLICK] The second pre-processing step indexes the nodes of the graph. The resulting index is used in the first main step of the pipeline, [CLICK] seeding, which aims to find seed matches between the query read and a region of the graph.
[CLICK] After optionally filtering these seed matches with a filtering, chaining, or clustering step, [CLICK] alignment is performed between all of the non-filtered seed locations within the graph and the query read to find the optimal alignment. Alignment is the most expensive step of the pipeline, so let’s look at it in detail.

## Slide 91: SeGraM Hardware Design
Host CPU
Main Memory (graph-based reference & index)
Main Memory (graph-based reference & index)
SeGraM Accelerator
MinSeed (MS)
Host CPU
Find Minimizers
query
read
1
BitAlign (BA)
Read
Scratchpad
Minimizer Scratchpad
Filter
Minimizers by Frequency
Seed Scratchpad
Find Candidate
Seed Regions
Input Scratchpad
Generate Bitvectors
Perform
Traceback
Bitvector Scratchpad
Hop Queues
query k-mers
minimizers
frequencies
seed locations
graph nodes
2
3
4
5
6
7
8
9
10
11
12
optimal alignment information
MinSeed: first hardware
accelerator for
Minimizer-based Seeding
BitAlign: first hardware accelerator for (Bitvector-based) sequence-to-graph Alignment
Notes: Let’s look at the overview of our hardware design.
[CLICK] Before SeGraM execution starts, as pre-processing steps, we (1) generate each chromosome’s graph structure, (2) index each graph’s nodes, and (3) pre-load both the resulting graph and hash table index into the main memory. Both the graph and its index are static data structures that can be generated only once and reused for multiple mapping executions.
[CLICK] SeGraM execution starts when the query read is streamed from the host and MinSeed writes it to the read scratchpad ( 1 ).
[CLICK] Using all of the k-length subsequences (i.e., k-mers) of the query read, [CLICK] MinSeed finds the minimum representative set of these k-mers (i.e., minimizers) according to a scoring mechanism and [CLICK] writes them to the minimizer scratchpad ( 2 ).
[CLICK] For each minimizer, MinSeed fetches its occurrence frequency from the hash table in main memory ( 3 ) and [CLICK] filters out each minimizer whose occurrence frequency is above a user-defined threshold ( 4 ). We aim to select the least frequent minimizers and filter out the most frequent minimizers such that we minimize the number of seed locations to be considered for the expensive alignment step.
[CLICK] Next, MinSeed fetches the seed locations of the remaining minimizers from main memory, and writes them to the seed scratchpad ( 5 ).
[CLICK] Finally, MinSeed calculates the candidate reference region (i.e., subgraph surrounding the seed) for each seed ( 6 ), [CLICK] fetches the graph nodes from memory for each candidate region in the reference and writes the nodes to the input scratchpad of BitAlign. ( 7 ).
[CLICK] BitAlign starts by reading the subgraph and the query read from the input scratchpad, and generates the bitvectors ( 8 ) required for performing approximate string matching and edit distance calculation.
While generating these bitvectors, [CLICK] BitAlign writes them to the hop queues ( 9 ) in order to handle the hops required for graph-based alignment, and also, [CLICK] to the bitvector scratchpad ( 10 ) to be later used as part of the traceback operation.
Once BitAlign finishes generating and writing all the bitvectors, [CLICK] it starts reading them back from the bitvector scratchpad, performs the traceback operation ( 11 ), finds the optimal alignment between the subgraph and the query read, and [CLICK] streams the optimal alignment information back to the host ( 12 ).

## Slide 92: Use Cases & Key Results
Sequence-to-Graph (S2G) Mapping
5.9×/106× speedup, 4.1×/3.0× less power than GraphAligner for long and short reads, respectively (state-of-the-art SW)
3.9×/742× speedup, 4.4×/3.2× less power than vg for long and short reads, respectively (state-of-the-art SW)
Sequence-to-Graph (S2G) Alignment
41×–539× speedup over PaSGAL with AVX-512 support (state-of-the-art SW)
Sequence-to-Sequence (S2S) Alignment
1.2×/4.8× higher throughput than GenASM and GACT of Darwin for long reads (state-of-the-art HW)
1.3×/2.4× higher throughput than GenASM and SillaX of GenAX for short reads (state-of-the-art HW)
Notes: [CLICK] [CLICK] [CLICK] We demonstrate that SeGraM provides significant improvements for multiple steps of the sequence-to-graph (i.e., S2G) and sequence-to-sequence (i.e., S2S) mapping pipelines.
==================================================================================================================
[CLICK] We show that (1) SeGraM provides greatly higher throughput and lower power consumption on both short and long reads compared to state-of-the-art software tools for sequence-to-graph mapping, and
[CLICK] (2) BitAlign significantly outperforms a state-of-the-art sequence-to-graph alignment tool and [CLICK] three state-of-the-art hardware solutions that are specifically designed for sequence-to-sequence alignment.
===========================================================================================================
We also show that MinSeed can be employed for the seeding step of both sequence-to-graph and sequence-to-sequence mapping pipelines.

## Slide 93: SeGraM Talk Video
https://www.youtube.com/watch?v=gyjqYoyDP9s

## Slide 94: Accelerating Sequence-to-Graph Mapping
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 95: Designing & Accelerating Basecallers
https://arxiv.org/pdf/2211.03079.pdf

## Slide 96: How Does a Nanopore Machine Work?
Nanopore is a nano-scale hole (<20nm).
In nanopore sequencers, an ionic current passes through the nanopores
When the DNA strand passes through the nanopore, the sequencer measures the the change in current
This change is used to identify the bases in the strand with the help of different electrochemical structures of the different bases
graphene nanopore
DNA strand
Figure is adapted from: https://phys.org/news/2013-12-gene-sequencing-future.html

## Slide 97: Accelerating Basecallers: Software Methods
M. Banu Cavlak, Gagandeep Singh, Mohammed Alser, Can Firtina, Joel Lindegger, Mohammad Sadrosadati, Nika Mansouri Ghiasi, Can Alkan, and Onur Mutlu, "TargetCall: Eliminating the Wasted Computation in Basecalling via Pre-Basecalling Filtering" Proceedings of the 21st Asia Pacific Bioinformatics Conference (APBC), Changsha, China, April 2023. [TargetCall Source Code] [arxiv.org Version] [Talk Video at BIO-Arch 2023 Workshop]
https://arxiv.org/pdf/2301.09200.pdf

## Slide 98: New Frontiers: Raw Signal Analysis
Can Firtina, Nika Mansouri Ghiasi, Joel Lindegger, Gagandeep Singh, Meryem Banu Cavlak, Haiyu Mao, and Onur Mutlu, "RawHash: Enabling Fast and Accurate Real-Time Analysis of Raw Nanopore Signals for Large Genomes" Proceedings of the 31st Annual Conference on Intelligent Systems for Molecular Biology and the 22nd European Conference on Computational Biology (ISMB/ECCB), Lyon, France, July 2023. [RawHash Source Code]
https://arxiv.org/pdf/2301.09200.pdf

## Slide 99: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 100: Process Data Where It Makes Sense
https://www.gsmarena.com/apple_announces_m1_ultra_with_20core_cpu_and_64core_gpu-news-53481.php
Apple M1 Ultra System (2022)
DRAM
DRAM
A lot of
SRAM
Storage
Storage
Sensors

## Slide 101: Goal: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processors & communication units?
  software & hardware interfaces?
  system software, compilers, languages?
  algorithms & theoretical foundations?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 102: Read Mapping & Filtering in Memory
We need to design
mapping & filtering algorithms
that fit processing-in-memory

## Slide 103: Near-Memory Pre-Alignment Filtering
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]

## Slide 104: Near-Memory SneakySnake
Problem: Read mapping is heavily bottlenecked by data movement from main memory
Solution: Perform read mapping near where data resides using specialized logic
We carefully redesign the accelerator logic of SneakySnake to exploit near-memory computation capability on real FPGA boards that use HBM (high-bandwidth memory)
Near-memory SneakySnake improves performance and energy efficiency by 27.4× and 133×, respectively, over a 16-core (64-thread) IBM POWER9 CPU

## Slide 105: Near-Memory Acceleration using FPGAs
IBM POWER9 CPU
HBM-based FPGA board
OCAPI
Source: AlphaData
Source: IBM
Near-HBM FPGA-based accelerator
Two communication technologies: CAPI2 and OCAPI
Two memory technologies: DDR4 and HBM
Two workloads: Weather Modeling and Genome Analysis
Notes: To this end we build a [CLICK] near-HBM FPGA based accelerator which is connected to a server-grade IBM POWER9-based CPU system

## Slide 106: Performance & Energy Greatly Improve
5-27× performance vs. a 16-core (64-thread) IBM POWER9 CPU
HBM alleviates memory bandwidth contention vs. DDR4
12-133× energy efficiency vs. a 16-core (64-thread) IBM POWER9 CPU
Notes: [CLICK]

## Slide 107: More On Near-Memory SneakySnake
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]

## Slide 108: Location Filtering in 3D-Stacked PIM
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" BMC Genomics, 2018. Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. [Slides (pptx) (pdf)] [Source Code] [arxiv.org Version (pdf)] [Talk Video at AACBB 2019]

## Slide 109: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 110: In-Storage Genome Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 111: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement from Storage
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 112: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 113: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 114: Filtering Opportunities
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate and short
  Long reads: less accurate and long
High sequencing error rates (long reads) or
High genetic variation (short or long reads)
Non-matching reads
Do not have potential matching locations, so they skip alignment
Low sequencing error rates (short reads) combined with
Low genetic variation
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Reads that do not require the expensive alignment step:
Notes: Let’s take a look at filtering opportunities based on the input reads.
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate (99.9%) and short (e.g., up to a few hundreds of DNA characters)
  Long reads: less accurate (85-90%) and long (e.g., from hundreds to millions of DNA characters)
Based on these, We leverage two filtering opportunities
First, we can filter exactly matching reads, which are reads that match exactly to one or more subsequences of the reference genome and do not require approximate string matching during alignment. Exact matches can frequently occur in short read sets with low sequencing errors and low genetic variations
Second, we can filter non-matching reads. Such reads do not have any potential matching locations in the reference genome can skip the expensive alignment step. Non-matching reads can frequently occur in long read sets with high sequencing errors and short or long read sets with high genetic variations

## Slide 115: Challenges
Read mapping workloads can exhibit different behavior
There are limited hardware resources
in the storage system
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD. By addressing these challenges [CLICK]

## Slide 116: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 117: In-Storage Genome Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 118: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 119: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 120: More on Processing-in-Memory
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 121: A Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=H3sEaINPBOE

## Slide 122: Tutorial on Processing in Memory
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=4x9nujJtqjM

## Slide 123: PIM Course (Fall 2022)
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=processing_in_memory
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=QLL0wQ9I4Dw&list=PL5Q2soXY2Zi8KzG2CQYRNQOVD0GOBrnKy
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 124: Processing-in-Memory Landscape Today
[UPMEM 2019]
[Samsung 2021]
[SK Hynix 2022]
[Samsung 2021]
This does not include many experimental chips and startups
[Alibaba 2022]

## Slide 125: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 126: UPMEM Memory Modules
E19: 8 chips DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 127: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 128: More on the UPMEM PIM System
https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=26

## Slide 129: SRC TECHCON Presentation
Dr. Juan Gomez-Luna
  Benchmarking Memory-Centric Computing Systems: Analysis of Real Processing-in-Memory Hardware
  Based on two major works
    https://arxiv.org/pdf/2105.03814.pdf
    https://arxiv.org/pdf/2207.07886.pdf
https://www.youtube.com/watch?v=nphV36SrysA

## Slide 130: UPMEM PIM System Summary & Analysis
Juan Gomez-Luna, Izzat El Hajj, Ivan Fernandez, Christina Giannoula, Geraldo F. Oliveira, and Onur Mutlu, "Benchmarking Memory-Centric Computing Systems: Analysis of Real Processing-in-Memory Hardware" Invited Paper at Workshop on Computing with Unconventional Technologies (CUT), Virtual, October 2021. [arXiv version] [PrIM Benchmarks Source Code] [Slides (pptx) (pdf)] [Talk Video (37 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 131: ML Training on Real PIM Systems
Juan Gómez Luna, Yuxin Guo, Sylvan Brocard, Julien Legriel, Remy Cimadomo, Geraldo F. Oliveira, Gagandeep Singh, and Onur Mutlu, "Evaluating Machine Learning Workloads on Memory-Centric Computing Systems" Proceedings of the 2023 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), Raleigh, North Carolina, USA, April 2023. [arXiv version, 16 July 2022.] [PIM-ML Source Code] Best paper session.
https://arxiv.org/pdf/2207.07886.pdf
https://github.com/CMU-SAFARI/pim-ml

## Slide 132: Sequence Alignment on Real PIM Systems
Safaa Diab, Amir Nassereldine, Mohammed Alser, Juan Gómez Luna, Onur Mutlu, and Izzat El Hajj, "A Framework for High-throughput Sequence Alignment using Real Processing-in-Memory Systems" Bioinformatics, [published online on] 27 March 2023. [Online link at Bioinformatics Journal] [arXiv preprint] [AiM Source Code]
https://arxiv.org/pdf/2208.01243.pdf
https://github.com/CMU-SAFARI/alignment-in-memory

## Slide 133
Sequence alignment on traditional systems is limited by the memory bandwidth bottleneck
Processing-in-memory (PIM) overcomes this bottleneck by placing cores near the memory
Our framework, Alignment-in-Memory (AIM), is a PIM framework that supports multiple alignment algorithms (NW, SWG, GenASM, WFA)
  Implemented on UPMEM, the first real PIM system
Results show substantial speedups over both CPUs (1.8X-28X) and GPUs (1.2X-2.7X)
AIM is available at:
  https://github.com/CMU-SAFARI/alignment-in-memory
Summary

## Slide 134: Accelerating Basecalling + Read Mapping via PIM
Haiyu Mao, Mohammed Alser, Mohammad Sadrosadati, Can Firtina, Akanksha Baranwal, Damla Senol Cali, Aditya Manglik, Nour Almadhoun Alserr, and Onur Mutlu, "GenPIP: In-Memory Acceleration of Genome Analysis via Tight Integration of Basecalling and Read Mapping" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (25 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.08600.pdf

## Slide 135: Genome Analysis Pipeline
High-quality
Read
G
G
A
C
Compute
Storage
Storage
1. Basecalling
Compute
2. Read Quality Control
Storage
Store
mapping results
Genome sequencing
A
T
G
C
G
T
T
C
T
C
A
A
A
G
Compute
3. Read Mapping
Reference genome
T
A
T
G
G
A
C
T
T
T
A
G
C
A
A
A
C
T
C
A
A
A
G
G
C
G
T
T
C
A
T
G
G
A
C
A
T
G
G
A
C
G
C
G
T
T
C
Mapped
Unmapped
Low-quality
Notes: After we get the raw signals from the nanopore sequencing machine, we store them
Then we execute the first step, basecalling. we read the raw signals chunk by chunk from the storage and basecall them one by one into chunk of bases.
Here, red means the base quality is low and green means the base quality is high
After basecalling all chunks in a sequence, we assemble them into a read.
After basecalling all raw signal sequences into reads, we store them
Then execute the second step, read quality control.
Read quality control filters out the low-quality reads
And stores the high-quality reads
After that, we execute the read mapping step to map the read to the reference genome
If the read cannot be mapped to the reference genome, we discard it
For the read can be mapped to the reference genome, we store the mapping results.

## Slide 136: Limitation 1: Large Data Movement
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
Large data movement between genome analysis steps
3913 GB
546 GB
437 GB
382 GB
Using a human dataset in [NC’19] as an example:
[NC'19] Rory Bowden, Robert W Davies, Andreas Heger, Alistair T Pagnamenta, Mariateresa de Cesare, Laura E Oikkonen, Duncan Parkes, Colin Freeman, Fatima Dhalla, Smita Y Patel, et al. Sequencing of human genomes with nanopore technology. Nature Communications, 2019.
Notes: The genome analysis pipeline has two main limitations
The first one is large data movement
We use a human dataset as an example
We move the raw signals to the basecalling
Then store the reads
And move the reads to the machine that executes read quality control
Then move the high quality reads to machines executes read mapping
In the end, only mapped reads are reviewed by bio analysts.
We conclude that there is large data movement between these steps

## Slide 137: Limitation 2: Wasted Computation
Using a human dataset in [NC’19] as an example:
Raw Signals
Basecalling
Reads
Read quality
control
High-quality
reads
Read
mapping
Mapped
reads
Low-quality
reads
Unmapped
reads
A considerable amount of computation on useless data due to
Low-quality reads
Unmapped reads
100%
79.5%
69.5%
20.5%
10%
[NC'19] Rory Bowden, Robert W Davies, Andreas Heger, Alistair T Pagnamenta, Mariateresa de Cesare, Laura E Oikkonen, Duncan Parkes, Colin Freeman, Fatima Dhalla, Smita Y Patel, et al. Sequencing of human genomes with nanopore technology. Nature Communications, 2019.
Notes: Second, 100% of reads are basecalled but 20.5% low-quality reads are filtered
And 10% of unmapped reads are discarded.
We conclude that there is a considerable amount of computation on useless data due to low quality reads and unmapped reads

## Slide 138: Overview: Two Limitations
Multiple steps in genome analysis
Large data movement between multiple steps
A lot of
wasted computation done on data that is later discovered to be useless
Notes: [CLICK] There are multiple steps in the genome analysis
[CLICK] We observe there is large data movement between these steps
[CLICK] and a lot of wasted computation done on the data that later discovered to be useless

## Slide 139: Overview: GenPIP
GenPIP: A fast and energy-efficient in-memory acceleration system for the Genome analysis PIPeline via tight integration of genome analysis steps
GenPIP has two key techniques
GenPIP outperforms state-of-the-art software & hardware solutions using CPU, GPU, and optimistic PIM by 41.6×, 8.4x, and 1.4x, respectively.
  Early rejection (ER)
    Timely stops the execution on useless data by predicting which reads will not be useful
  Chunk-based pipeline (CP)
    Provides fine-grained collaboration of genome analysis steps
Notes: To overcome these two limitations, we propose GenPIP
[CLICK] GenPIP is A fast and energy-efficient in-memory acceleration system for the Genome analysis PIPeline via tight integration of genome analysis steps
[CLICK] GenPIP has two key techniques
    A chunk-based pipeline that provides fine-grained collaboration of genome analysis steps
    An early-rejection technique predicts which reads will not be useful and then stops the execution of basecalling and read mapping for such reads
[CLICK] GenPIP outperforms state-of-the-art software & hardware solutions.

## Slide 140: Goal and Opportunities
Chart: Normalized Speedup
| System A | System B | System C
Normalized Speedup | 2.7 | 6.1 | 9
We perform a study to quantify potential performance benefits
  Results are normalized to the performance of GPU
Goal: Efficiently accelerate the entire genome analysis pipeline while minimizing data movement and useless computation
NVM-based PIM accelerators for separate basecalling and read mapping
no data movement
between the accelerators of analysis steps
no data movement
and
no useless reads
(ideal case)
Notes: Our goal in this work is to efficiently accelerate the entire genome analysis pipeline while minimizing data movement and useless computation
To quantify potential benefits of overcoming the two limitations, we compare performance of the three systems and results are normalized to the performance of GPU
First, Basecalling and read mapping are executed in two in-memory accelerators separately, which achieves 2.7 times speedup
Assume there is no data movement, which achieves 6.1 times speedup
Assume there is no data movement and no useless reads in the pipeline. Which achieves 9 times speedup

## Slide 141: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 142: Newer Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version] [Slides (pptx) (pdf)] [Talk Video at AACBB 2019]
Oxford Nanopore MinION

## Slide 143: New Applications: Graph Genomes
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 144: New Applications: Frequent Reference Updates
Jeremie S. Kim, Can Firtina, M. Banu Cavlak, Damla Senol Cali, Nastaran Hajinazar, Mohammed Alser, Can Alkan, and Onur Mutlu, "AirLift: A Fast and Comprehensive Technique for Remapping Alignments between Reference Genomes" Proceedings of the 21st Asia Pacific Bioinformatics Conference (APBC), Changsha, China, April 2023. [AirLift Source Code] [arxiv.org Version (pdf)] [Talk Video at BIO-Arch 2023 Workshop]
https://arxiv.org/pdf/1912.08735.pdf

## Slide 145: Mapping Constant Regions Between References
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Can Alkan, and Onur Mutlu, "FastRemap: A Tool for Quickly Remapping Reads between Genome Assemblies" Bioinformatics, btac554. [FastRemap Source Code]
https://arxiv.org/pdf/2201.06255.pdf

## Slide 146: New Frontiers: Raw Signal Analysis
Can Firtina, Nika Mansouri Ghiasi, Joel Lindegger, Gagandeep Singh, Meryem Banu Cavlak, Haiyu Mao, and Onur Mutlu, "RawHash: Enabling Fast and Accurate Real-Time Analysis of Raw Nanopore Signals for Large Genomes" Proceedings of the 31st Annual Conference on Intelligent Systems for Molecular Biology and the 22nd European Conference on Computational Biology (ISMB/ECCB), Lyon, France, July 2023. [RawHash Source Code]
https://arxiv.org/pdf/2301.09200.pdf

## Slide 147: New Frontiers: Raw Signal Analysis
M. Banu Cavlak, Gagandeep Singh, Mohammed Alser, Can Firtina, Joel Lindegger, Mohammad Sadrosadati, Nika Mansouri Ghiasi, Can Alkan, and Onur Mutlu, "TargetCall: Eliminating the Wasted Computation in Basecalling via Pre-Basecalling Filtering" Proceedings of the 21st Asia Pacific Bioinformatics Conference (APBC), Changsha, China, April 2023. [TargetCall Source Code] [arxiv.org Version] [Talk Video at BIO-Arch 2023 Workshop]
https://arxiv.org/pdf/2301.09200.pdf

## Slide 148: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 149: Conclusion

## Slide 150: Things Are Happening In Industry

## Slide 151: Illumina DRAGEN Bio-IT Platform (2018)
Processes whole genome at 30x coverage in ~25 minutes with hardware support for data compression
FPGA board(s)
emea.illumina.com/products/by-type/informatics-products/dragen-bio-it-platform.html
emea.illumina.com/company/news-center/press-releases/2018/2349147.html

## Slide 152: NVIDIA Clara Parabricks (2020)
https://developer.nvidia.com/clara-parabricks
GPU board(s)
A University of Michigan startup in 2018 joined NVIDIA in 2020

## Slide 153: NVIDIA Hopper DPX Instructions (2022)
https://blogs.nvidia.com/blog/2022/03/22/nvidia-hopper-accelerates-dynamic-programming-using-dpx-instructions/

## Slide 154: Bionano & NVIDIA: Accelerating Analysis for Fast Time to Results
We are accelerating the transformation in how we analyze the human genome!
New high-performance algorithms from Bionano
  Analysis of highly complex cancer
  whole genomes in less than 2 hours
Technological solution to support higher throughput
Powered by NVIDIA RTX™ 6000
Ada Generation GPUs
Workflow tailored for a small lab and
IT footprint
Notes: Partnership
Designed to scale from small labs that do not have datacenters to datacenters and cloud

## Slide 155: Recall Our Dream (from 2007)
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
Still a long ways to go
  Energy efficiency
  Performance (latency)
  Security & privacy
  Huge memory bottleneck

## Slide 156: Conclusion
System design for bioinformatics is a critical problem
  It has large scientific, medical, societal, personal implications
This talk is about accelerating a key step in bioinformatics: genome sequence analysis
  Especially techniques for read mapping
We covered various recent ideas to accelerate read mapping
  My personal journey since September 2006
Many future opportunities exist
  Especially with new sequencing technologies
  Especially with new applications and use cases

## Slide 157: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 158: A Longer Version of This Talk (I)
https://www.youtube.com/watch?v=NCagwf0ivT0

## Slide 159: A Longer Version of This Talk (II)
https://www.youtube.com/watch?v=tVpg0XqU_c4

## Slide 160: Genomics Course (Fall 2022)
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=bioinformatics
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=bioinformatics
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=nA41964-9r8&list=PL5Q2soXY2Zi8tFlQvdxOdizD_EhVAMVQV
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=DEL_5A_Y3TI&list=PL5Q2soXY2Zi8NrPDgOR1yRU_Cxxjw-u18
Project course
  Taken by Bachelor’s/Master’s students
  Genomics lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 161: PIM Course (Fall 2022)
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=processing_in_memory
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=QLL0wQ9I4Dw&list=PL5Q2soXY2Zi8KzG2CQYRNQOVD0GOBrnKy
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 162: SSD Course (Spring 2023)
Spring 2023 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2023/doku.php?id=modern_ssds
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=modern_ssds
Youtube Livestream (Spring 2023):
  https://www.youtube.com/watch?v=4VTwOMmsnJY&list=PL5Q2soXY2Zi_8qOM5Icpp8hB2SHtm4z57&pp=iAQB
Youtube Livestream (Fall 2022):
  https://www.youtube.com/watch?v=hqLrd-Uj0aU&list=PL5Q2soXY2Zi9BJhenUq4JI5bwhAMpAp13&pp=iAQB
Project course
  Taken by Bachelor’s/Master’s students
  SSD Basics and Advanced Topics
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 163: Real PIM Tutorials [ISCA’23, ASPLOS’23, HPCA’23]
June, March, Feb : Lectures + Hands-on labs + Invited talks
https://events.safari.ethz.ch/isca-pim-tutorial/

## Slide 164: Real PIM Tutorial [ISCA 2023]
June 18: Lectures + Hands-on labs + Invited talks
https://events.safari.ethz.ch/isca-pim-tutorial/
https://www.youtube.com/live/GIb5EgSrWk0

## Slide 165: Real PIM Tutorial [ASPLOS 2023]
https://events.safari.ethz.ch/asplos-pim-tutorial/
March 26: Lectures + Hands-on labs + Invited talks
https://www.youtube.com/watch?v=oYCaLcT0Kmo

## Slide 166: Real PIM Tutorial [HPCA 2023]
February 26: Lectures + Hands-on labs + Invited Talks
https://www.youtube.com/watch?v=f5-nT1tbz5w
https://events.safari.ethz.ch/real-pim-tutorial/

## Slide 167: Acknowledgments
Think BIG, Aim HIGH!
https://safari.ethz.ch

## Slide 168
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 169: SAFARI Newsletter December 2021 Edition
https://safari.ethz.ch/safari-newsletter-december-2021/

## Slide 170: SAFARI Newsletter June 2023 Edition
https://safari.ethz.ch/safari-newsletter-june-2023/

## Slide 171
Think BIG, Aim HIGH!
https://www.youtube.com/watch?v=mV2OuB2djEs
SAFARI Introduction & Research
Computer architecture, HW/SW, systems, bioinformatics, security, memory

## Slide 172: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 173: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 174: Accelerating Genome Analysis via Algorithm-Architecture Co-Design
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
11 July 2023
DAC 2023 Special Session Talk

## Slide 175: Backup Slides for Further Info

## Slide 176: Our First Step: Comprehensive Mapping
+ Guaranteed to find all mappings  sensitive
+ Can tolerate up to e errors
http://mrfast.sourceforge.net/
Alkan+, "Personalized copy number and segmental duplication
maps using next-generation sequencing”, Nature Genetics 2009.
Notes: It turned out the Hash Table based mappers solve the first 2 challenges pretty well. They guarantee to find all mappings with no more than e errors present.

## Slide 177: Resources & Acknowledgments

## Slide 178: Special Research Sessions & Courses
Special Session at ISVLSI 2022: 9 cutting-edge talks
https://www.youtube.com/watch?v=qeukNs5XI3g

## Slide 179: Detailed Lectures on Genome Analysis
Computer Architecture, Fall 2020, Lecture 3a
  Introduction to Genome Sequence Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=CrRb32v7SJc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=5
Computer Architecture, Fall 2020, Lecture 8
  Intelligent Genome Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=ygmQpdDTL7o&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=14
Computer Architecture, Fall 2020, Lecture 9a
  GenASM: Approx. String Matching Accelerator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=XoLpzmN-Pas&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=15
Accelerating Genomics Project Course, Fall 2020, Lecture 1
  Accelerating Genomics (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=rgjl8ZyLsAg&list=PL5Q2soXY2Zi9E2bBVAgCqLgwiDRQDTyId
https://www.youtube.com/onurmutlulectures

## Slide 180: Comp Arch (Fall’21)
Fall 2021 Edition:
  https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Fall 2020 Edition:
  https://safari.ethz.ch/architecture/fall2020/doku.php?id=schedule
Youtube Livestream (2021):
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Youtube Livestream (2020):
  https://www.youtube.com/watch?v=c3mPdZA-Fmc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 181: DDCA (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2022/doku.php?id=schedule
Spring 2021 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2021/doku.php?id=schedule
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=cpXdE3HwvK0&list=PL5Q2soXY2Zi97Ya5DEUpMpO2bbAoaG7c6
Youtube Livestream (Spring 2021):
  https://www.youtube.com/watch?v=LbC0EZY8yw4&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN
Bachelor’s course
  2nd semester at ETH Zurich
  Rigorous introduction into “How Computers Work”
  Digital Design/Logic
  Computer Architecture
  10 FPGA Lab Assignments
https://www.youtube.com/onurmutlulectures

## Slide 182: Seminar in Comp Arch (Spring & Fall)
Spring 2022 Edition:
  https://safari.ethz.ch/architecture_seminar/spring2022/doku.php?id=schedule
Fall 2021 Edition:
  https://safari.ethz.ch/architecture_seminar/fall2021/doku.php?id=schedule
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=rS9UPk509AQ&list=PL5Q2soXY2Zi_hxizriwKmFHgcoe2Q8-m0
Youtube Livestream (Fall 2021):
  https://www.youtube.com/watch?v=4TcP297mdsI&list=PL5Q2soXY2Zi_7UBNmC9B8Yr5JSwTG9yH4
Critical analysis course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  20+ research papers, presentations, analyses

## Slide 183: Hetero. Systems (Spring’22)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=heterogeneous_systems
Youtube Livestream:
  https://www.youtube.com/watch?v=oFO5fTrgFIY&list=PL5Q2soXY2Zi9XrgXR38IM_FTjmY6h7Gzm
Project course
  Taken by Bachelor’s/Master’s students
  GPU and Parallelism lectures
  Hands-on research exploration
  Many research readings

## Slide 184: HW/SW Co-Design (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=hw_sw_codesign
Youtube Livestream:
  https://youtube.com/playlist?list=PL5Q2soXY2Zi8nH7un3ghD2nutKWWDk-NK
Project course
  Taken by Bachelor’s/Master’s students
  HW/SW co-design lectures
  Hands-on research exploration
  Many research readings

## Slide 185: Some Other Recent Papers

## Slide 186: Finding Approximate Seed Matches
Can Firtina, Jisung Park, Mohammed Alser, Jeremie S. Kim, Damla Senol Cali, Taha Shahroodi, Nika Mansouri-Ghiasi, Gagandeep Singh, Konstantinos Kanellopoulos, Can Alkan, and Onur Mutlu, "BLEND: A Fast, Memory-Efficient, and Accurate Mechanism to Find Fuzzy Seed Matches" Preprint in arXiv, 2021. [arXiv preprint] [BLEND Source Code and Data]

## Slide 187: Hardware Acceleration for pHMMs
Can Firtina, Kamlesh Pillai, Gurpreet S. Kalsi, Bharathwaj Suresh, Damla Senol Cali, Jeremie S. Kim, Taha Shahroodi, Meryem Banu Cavlak, Joel Lindegger, Mohammed Alser, Juan Gómez-Luna, Sreenivas Subramoney, and Onur Mutlu, "ApHMM: A Profile Hidden Markov Model Acceleration Framework for Genome Analysis" Preprint in arXiv, 2022. [Source Code]

## Slide 188: Remapping Reads Between References
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Nastaran Hajinazar, Mohammed Alser, Can Alkan, and Onur Mutlu, "AirLift: A Fast and Comprehensive Technique for Remapping Alignments between Reference Genomes" Preprint in arXiv and bioRxiv, 2021. [bioRxiv preprint] [arXiv preprint] [AirLift Source Code and Data]

## Slide 189: Mapping Constant Regions Between References
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Can Alkan, and Onur Mutlu, "FastRemap: A Tool for Quickly Remapping Reads between Genome Assemblies" Bioinformatics, btac554. [FastRemap Source Code]

## Slide 190: COVIDHunter
Mohammed Alser, Jeremie S. Kim, Nour Almadhoun Alserr, Stefan W. Tell,
Onur Mutlu
“COVIDHunter: COVID-19 Pandemic Wave Prediction and Mitigation via Seasonality Aware Modeling”
Frontiers in Public Health 2022
[Source Code]

## Slide 191: Packaging Omics Methods
Mohammed Alser, Sharon Waymost, Ram Ayyala, Brendan Lawlor, Richard J. Abdill, Neha Rajkumar, Nathan LaPierre, Jaqueline Brito, Andre M. Ribeiro-dos-Santos, Can Firtina, Nour Almadhoun, Varuni Sarwal, Eleazar Eskin, Qiyang Hu, Derek Strong, Byoung-Do (BD)Kim, Malak S. Abedalthagafi, Onur Mutlu, Serghei Mangul
“Packaging, containerization, and virtualization of computational omics methods: Advances, challenges, and opportunities”
arrXiv 2022

## Slide 192: Demeter (HD Food Microbiome Profiling)
Taha Shahroodi, Mahdi Zahedi, Can Firtina, Mohammed Alser, Stephan Wong,
Onur Mutlu, Said Hamdioui
“Demeter: A Fast and Energy-Efficient Food Profiler using Hyperdimensional Computing in Memory”
IEEE Access, 2022

## Slide 193: End of Backup Slides