## Slide 1: Future Computing Platforms Challenges and Opportunities
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
10 November 2021
EdukCircle Intl. Conv. on Engineering & Computer Technology

## Slide 2: Current Research Mission
Computer architecture, HW/SW, systems, bioinformatics, security
Graphics and Vision Processing
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
Build fundamentally better architectures
Notes: Professor Mutlu’s research focus is all aspects of computer architecture, HW/SW interaction and bioinformatics.
He is looking for students to perform research in these areas.
He and his group, SAFARI, solve fundamental problems spanning:
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
His group does broad research spanning systems to logic with architecture at center

## Slide 3: Four Key Current Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency and Predictable Architectures
Architectures for AI/ML, Genomics, Medicine, Health

## Slide 4: The Transformation Hierarchy
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (narrow view)
Computer Architecture (expanded view)

## Slide 5: Axiom
To achieve the highest energy efficiency and performance:
we must take the expanded view
of computer architecture
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Co-design across the hierarchy:
Algorithms to devices
Specialize as much as possible
within the design goals

## Slide 6: Current Research Mission & Major Topics
Data-centric arch. for low energy & high perf.
  Proc. in Mem/DRAM, NVM, unified mem/storage
Low-latency & predictable architectures
  Low-latency, low-energy yet low-cost memory
  QoS-aware and predictable memory systems
Fundamentally secure/reliable/safe arch.
  Tolerating all bit flips; patchable HW; secure mem
Architectures for ML/AI/Genomics/Health/Med
  Algorithm/arch./logic co-design; full heterogeneity
Data-driven and data-aware architectures
  ML/AI-driven architectural controllers and design
  Expressive memory and expressive systems
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Build fundamentally better architectures
Broad research
spanning apps, systems, logic
with architecture at the center

## Slide 7
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-april-2020/

## Slide 8: SAFARI Newsletter January 2021 Edition
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 9: Research & Teaching: Some Overview Talks
https://www.youtube.com/onurmutlulectures
Future Computing Architectures
  https://www.youtube.com/watch?v=kgiZlSOcGFM&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=1
Enabling In-Memory Computation
  https://www.youtube.com/watch?v=njX_14584Jw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=16
Accelerating Genome Analysis
  https://www.youtube.com/watch?v=r7sn41lH-4A&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=41
Rethinking Memory System Design
  https://www.youtube.com/watch?v=F7xZLNMIY1E&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=3
Intelligent Architectures for Intelligent Machines
  https://www.youtube.com/watch?v=c6_LgzuNdkw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=25
The Story of RowHammer
  https://www.youtube.com/watch?v=sgd7PHQQ1AI&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=39

## Slide 10: A Talk on Impactful Research & Teaching
https://www.youtube.com/watch?v=83tlorht7Mc&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=54

## Slide 11: An Interview on Computing Futures
https://www.youtube.com/watch?v=8ffSEKZhmvo

## Slide 12: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 13: Future Computing Platforms Challenges and Opportunities

## Slide 14: Why Do We Do Computing?

## Slide 15: Answer
To Solve Problems

## Slide 16: Answer Reworded
To Gain Insight
Hamming, “Numerical Methods for Scientists and Engineers,” 1962.

## Slide 17: Answer Extended
To Enable
a Better Life & Future

## Slide 18: How Does a Computer Solve Problems?

## Slide 19: Answer
Orchestrating Electrons
In today’s dominant technologies

## Slide 20: How Do Problems Get Solved by Electrons?

## Slide 21: The Transformation Hierarchy
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (narrow view)
Computer Architecture (expanded view)

## Slide 22: Computer Architecture
is the science and art of designing computing platforms (hardware, interface, system SW, and programming model)
to achieve a set of design goals
  E.g., highest performance on earth on workloads X, Y, Z
  E.g., longest battery life at a form factor that fits in your pocket with cost < $$$ CHF
  E.g., best average performance across all known workloads at the best performance/cost ratio
  …
  Designing a supercomputer is different from designing a smartphone  But, many fundamental principles are similar

## Slide 23: Different Platforms, Different Goals
Source: http://www.sia-online.org (semiconductor industry association)

## Slide 24: Different Platforms, Different Goals
Source: https://iq.intel.com/5-awesome-uses-for-drone-technology/

## Slide 25: Different Platforms, Different Goals
Source: https://taxistartup.com/wp-content/uploads/2015/03/UK-Self-Driving-Cars.jpg

## Slide 26: Different Platforms, Different Goals
Source: http://sm.pcmag.com/pcmag_uk/photo/g/google-self-driving-car-the-guts/google-self-driving-car-the-guts_dwx8.jpg

## Slide 27: Different Platforms, Different Goals
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 28: Different Platforms, Different Goals
Source: http://datacentervoice.com/wp-content/uploads/2015/10/data-center.jpg

## Slide 29: Different Platforms, Different Goals
Source: https://fossbytes.com/wp-content/uploads/2015/06/Supercomputer-TIANHE2-china.jpg

## Slide 30: Different Platforms, Different Goals
Jouppi et al., “In-Datacenter Performance Analysis of a Tensor Processing Unit”, ISCA 2017.

## Slide 31: Different Platforms, Different Goals
250 TFLOPS per chip in 2021
vs 90 TFLOPS in TPU3
1 ExaFLOPS per board
New ML applications (vs. TPU3):
Computer vision
Natural Language Processing (NLP)
Recommender system
Reinforcement learning that plays Go
https://spectrum.ieee.org/tech-talk/computing/hardware/heres-how-googles-tpu-v4-ai-chip-stacked-up-in-training-tests
Notes: For an image classification task, 256 Google TPUv4’s performance is nearly as fast as 768 Nvidia A100 graphics cards combined with 192 AMD Epyc 7742 CPU cores and 512 of Huawei’s AI-optimized Ascend910 chips paired with 128 Intel Xeon Platinum 8168 cores.
https://venturebeat.com/2021/05/18/google-details-new-ai-accelerator-chips/

## Slide 32: Different Platforms, Different Goals
ML accelerator: 260 mm2, 6 billion transistors, 600 GFLOPS GPU, 12 ARM 2.2 GHz CPUs.
Two redundant chips for better safety.
https://youtu.be/Ucp0TTmvqOE?t=4236

## Slide 33: Cerebras’s Wafer Scale Engine (2019)
Cerebras WSE
1.2 Trillion transistors
46,225 mm2
Largest GPU
21.1 Billion transistors
815 mm2
The largest ML
accelerator chip
400,000 cores
NVIDIA TITAN V
https://www.anandtech.com/show/14758/hot-chips-31-live-blogs-cerebras-wafer-scale-deep-learning
https://www.cerebras.net/cerebras-wafer-scale-engine-why-we-need-big-chips-for-deep-learning/
Notes: The Wafer-Scale Engine is the most massive AI chip ever produced and packs a whopping 400,000 cores in a 46,225mm2 footprint.

## Slide 34: Cerebras’s Wafer Scale Engine-2 (2021)
Cerebras WSE-2
2.6 Trillion transistors
46,225 mm2
Largest GPU
54.2 Billion transistors
826 mm2
The largest ML
accelerator chip (2021)
850,000 cores
NVIDIA Ampere GA100
https://www.anandtech.com/show/14758/hot-chips-31-live-blogs-cerebras-wafer-scale-deep-learning
https://www.cerebras.net/cerebras-wafer-scale-engine-why-we-need-big-chips-for-deep-learning/

## Slide 35: Many (Other) AI/ML Chips
Alibaba
Amazon
Facebook
Google
Huawei
Intel
Microsoft
NVIDIA
Tesla
Many Others and Many Startups are Building Their Own Chips…
Many More to Come…

## Slide 36: Many (Other) AI/ML Chips (2019)
Alibaba
Amazon
Facebook
Google
Huawei
Microsoft
NVIDIA
Tesla
Many Startups…
Many More to Come…
https://basicmi.github.io/AI-Chip/

## Slide 37: Many (Other) AI/ML Chips (2021)
Alibaba
Amazon
Facebook
Google
Huawei
Microsoft
NVIDIA
Tesla
Many Startups…
Many More to Come…
https://basicmi.github.io/AI-Chip/

## Slide 38: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 39: Experimental Analysis of the UPMEM PIM Engine
https://arxiv.org/pdf/2105.03814.pdf

## Slide 40: UPMEM Memory Modules
E19: 8 chips DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 41: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 42: Understanding a Modern PIM Architecture
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 43: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 44: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=Pp9jSU2b9oM&list=PL5Q2soXY2Zi8_VVChACnON4sfh2bJ5IrD&index=159

## Slide 45: FPGA-based Processing Near Memory
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), to appear, 2021.

## Slide 46: Samsung Function-in-Memory DRAM (2021)
https://news.samsung.com/global/samsung-develops-industrys-first-high-bandwidth-memory-with-ai-processing-power

## Slide 47: Samsung Function-in-Memory DRAM (2021)

## Slide 48: Future of Genome Sequencing & Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 49: Axiom
To achieve the highest energy efficiency and performance:
we must take the expanded view
of computer architecture
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Co-design across the hierarchy:
Algorithms to devices
Specialize as much as possible
within the design goals

## Slide 50: What Kind of a Future Do We Want?

## Slide 51: How Reliable/Secure/Safe is This Bridge?
Source: http://www.technologystudent.com/struct1/tacom1.png

## Slide 52: Collapse of the “Galloping Gertie”
Source: AP
http://www.wsdot.wa.gov/tnbhistory/connections/connections3.htm

## Slide 53: Another View
Source: AP
Source: http://www.seattlepi.com/science/article/A-Tacoma-Narrows-Galloping-Gertie-bridge-6617030.php

## Slide 54: How Secure Are These People?
Source: https://s-media-cache-ak0.pinimg.com/originals/48/09/54/4809543a9c7700246a0cf8acdae27abf.jpg
Security is about preventing unforeseen consequences

## Slide 55: How Safe & Secure Is This Platform?
Source: https://taxistartup.com/wp-content/uploads/2015/03/UK-Self-Driving-Cars.jpg

## Slide 56: Challenge and Opportunity for Future
Reliable, Secure, Safe

## Slide 57: Do We Want This?
Source: V. Milutinovic

## Slide 58: Or This?
Source: V. Milutinovic

## Slide 59: Challenge and Opportunity for Future
Sustainable
and
Energy Efficient

## Slide 60: Many Difficult Problems: Climate
Source: https://farm9.staticflickr.com/8571/16376102935_8628150df8_o.jpg

## Slide 61: Many Difficult Problems: Congestion
Source: https://blogs-images.forbes.com/jimgorzelany/files/2015/10/China-G4-backup-this-oct-reuters.jpg

## Slide 62: Many Difficult Problems: Intelligence
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 63: Many Difficult Problems: Public Health
Source: https://blog.wego.com/7-crowded-places-and-events-that-you-will-love/

## Slide 64: Many Difficult Problems: Genome Analysis
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 65: Accelerating Genome Analysis
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 66: GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 67: Future of Genome Sequencing & Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 68: More on Fast & Efficient Genome Analysis
Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" Invited Lecture at Technion, Virtual, 26 January 2021. [Slides (pptx) (pdf)] [Talk Video (1 hour 37 minutes, including Q&A)] [Related Invited Paper (at IEEE Micro, 2020)]

## Slide 69: Detailed Lectures on Genome Analysis
Computer Architecture, Fall 2020, Lecture 3a
  Introduction to Genome Sequence Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=CrRb32v7SJc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=5
Computer Architecture, Fall 2020, Lecture 8
  Intelligent Genome Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=ygmQpdDTL7o&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=14
Computer Architecture, Fall 2020, Lecture 9a
  GenASM: Approx. String Matching Accelerator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=XoLpzmN-Pas&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=15
Accelerating Genomics Project Course, Fall 2020, Lecture 1
  Accelerating Genomics (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=rgjl8ZyLsAg&list=PL5Q2soXY2Zi9E2bBVAgCqLgwiDRQDTyId
https://www.youtube.com/onurmutlulectures

## Slide 70: Challenge and Opportunity for Future
High Performance
(to solve
the toughest & all problems)

## Slide 71: Personalized Medicine
Source: Jane Ades, NHGRI

## Slide 72: Comparative Genomics
Source: By Aaron E. Darling, István Miklós, Mark A. Ragan - Figure 1 from Darling AE, Miklós I, Ragan MA (2008).
"Dynamics of Genome Rearrangement in Bacterial Populations". PLOS Genetics. DOI:10.1371/journal.pgen.1000128., CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=30550950

## Slide 73: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION

## Slide 74: Challenge and Opportunity for Future
Personalized and Private
(in every aspect of life:
health, medicine,
spaces, devices, robotics, …)

## Slide 75: This Lecture is About …
Questioning what limits us in designing the best computing architectures for the future
Providing directions for fundamentally better designs
Advocating principled approaches

## Slide 76: Increasingly Demanding Applications
Dream…
and, they will come
As applications push boundaries, computing platforms will become increasingly strained.

## Slide 77: Key Realization

## Slide 78: Realization
Modern Systems are Bottlenecked by
Data Storage
and Movement

## Slide 79: Focus is on Data Storage Systems (Memory)
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processors
and caches
Main Memory
Storage (SSD/HDD)

## Slide 80: Focus is on Data Storage Systems (Memory)
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
FPGAs

## Slide 81: Focus is on Data Storage Systems (Memory)
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
GPUs

## Slide 82: The Problem
Computing
is Bottlenecked by Data

## Slide 83: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate more than we can process

## Slide 84: Memory Is Critical for Performance (I)
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 85: Memory Is Critical for Performance (I)
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Memory → bottleneck

## Slide 86: Memory Is Critical for Performance (II)
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 87: Memory Is Critical for Performance (II)
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Memory → bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 88
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 89
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Memory → bottleneck
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 90: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version]
Oxford Nanopore MinION

## Slide 91: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION
Memory → bottleneck

## Slide 92: Memory is Critical for Energy
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 93: Memory is Critical for Reliability
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
As memory
capacity increases, system reliability reduces

## Slide 94: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 95: Realization Reworded
Modern Systems are Bottlenecked by
Memory

## Slide 96: An “Early” Overview Paper…
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Proceedings of the 5th International Memory Workshop (IMW), Monterey, CA, May 2013. Slides (pptx) (pdf) EETimes Reprint
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 97: Four Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency and Predictable Architectures
Architectures for AI/ML, Genomics, Medicine, Health

## Slide 98: Maslow’s (Human) Hierarchy of Needs
We need to start with reliability, security, safety…
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.
Source: By User:Factoryjoe - Mazlow's Hierarchy of Needs.svg, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=7964065

## Slide 99: How Reliable/Secure/Safe is This Bridge?
Source: http://www.technologystudent.com/struct1/tacom1.png

## Slide 100: Collapse of the “Galloping Gertie”
Source: AP
http://www.wsdot.wa.gov/tnbhistory/connections/connections3.htm

## Slide 101: How Secure Are These People?
Source: https://s-media-cache-ak0.pinimg.com/originals/48/09/54/4809543a9c7700246a0cf8acdae27abf.jpg
Security is about preventing unforeseen consequences

## Slide 102: The Problem
We do not seem to have
design principles for
(guaranteeing)
reliability and security

## Slide 103: As Memory Scales, It Becomes Unreliable
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 104: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor must be large enough for long data retention time
As DRAM cell becomes smaller, it becomes more vulnerable

## Slide 105: Infrastructures to Understand Such Issues
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 106: Infrastructures to Understand Such Issues
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 107: SoftMC: Open Source DRAM Infrastructure
Hasan Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 108: SoftMC
https://github.com/CMU-SAFARI/SoftMC

## Slide 109: A Curious Discovery [Kim et al., ISCA 2014]
One can
predictably induce errors
in most DRAM memory chips

## Slide 110: DRAM RowHammer
A simple hardware failure mechanism
can create a widespread
system security vulnerability

## Slide 111: Modern DRAM is Prone to Disturbance Errors
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Hammered Row
Repeatedly reading a row enough times (before memory gets refreshed) induces disturbance errors in adjacent rows in most real DRAM chips you can buy today
Opened
Closed
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 112: Most DRAM Modules Are Vulnerable
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 113: Recent DRAM Is More Vulnerable
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 114: Recent DRAM Is More Vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 115: Recent DRAM Is More Vulnerable
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 116: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 117: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 118: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 119: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 120: Observed Errors in Real Systems
A real reliability & security issue
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: When we executed the code on four different processors, all four of them yielded errors. Intel Haswell has the most errors, at 23 thousand, because it has the highest rate of accessing DRAM.
Later on, I’ll show that we can induce as many as ten million disturbance errors in a more controlled environment.
From this, we conclude that disturbance errors are a serious reliability issue.

## Slide 121: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn+, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)

## Slide 122: RowHammer Security Attack Example
“Rowhammer” is a problem with some recent DRAM devices in which repeatedly accessing a row of memory can cause bit flips in adjacent rows (Kim et al., ISCA 2014).
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
We tested a selection of laptops and found that a subset of them exhibited the problem.
We built two working privilege escalation exploits that use this effect.
  Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn+, 2015)
One exploit uses rowhammer-induced bit flips to gain kernel privileges on x86-64 Linux when run as an unprivileged userland process.
When run on a machine vulnerable to the rowhammer problem, the process was able to induce bit flips in page table entries (PTEs).
It was able to use this to gain write access to its own page table, and hence gain read-write access to all of physical memory.
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn & Dullien, 2015)

## Slide 123: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 124: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 125: More Security Implications (I)
Source: https://lab.dsst.io/32c3-slides/7197.html
Rowhammer.js: A Remote Software-Induced Fault Attack in JavaScript (DIMVA’16)
“We can gain unrestricted access to systems of website visitors.”

## Slide 126: More Security Implications (II)
Source: https://fossbytes.com/drammer-rowhammer-attack-android-root-devices/
Drammer: Deterministic Rowhammer Attacks on Mobile Platforms, CCS’16
  “Can gain control of a smart phone deterministically”

## Slide 127: More Security Implications (III)
Using an integrated GPU in a mobile system to remotely escalate privilege via the WebGL interface

## Slide 128: More Security Implications (IV)
Rowhammer over RDMA (I)

## Slide 129: More Security Implications (V)
Rowhammer over RDMA (II)

## Slide 130: More Security Implications (VI)
IEEE S&P 2020

## Slide 131: More Security Implications (VII)
USENIX Security 2019

## Slide 132: More Security Implications (VIII)
USENIX Security 2020

## Slide 133: More Security Implications (IX)
Rowhammer on MLC NAND Flash (based on [Cai+, HPCA 2017])

## Slide 134: More Security Implications?

## Slide 135: Apple’s Patch for RowHammer
https://support.apple.com/en-gb/HT204934
HP, Lenovo, and other vendors released similar patches

## Slide 136: Solution Direction: Principled Designs
Design fundamentally secure
computing architectures
Predict and prevent
such safety issues

## Slide 137: Our Solution to RowHammer
PARA: Probabilistic Adjacent Row Activation
Key Idea
  After closing a row, we activate (i.e., refresh) one of its neighbors with a low probability: p = 0.005
Reliability Guarantee
  When p=0.005, errors in one year: 9.4×10-14
  By adjusting the value of p, we can vary the strength of protection against errors
Notes: We provide a more efficient solution, called PARA, which stands for probabilistic adjacent row activation.
The key idea is thus: after closing a row, we activate (i.e., refresh) one of its neighbors with a low probability, for example, p equal to 0.005.
PARA provides a strong reliability guarantee even under the worst-case access patterns to DRAM. When we set p to 0.005, the expected number of errors in one year is 9.4 times 10 to the negative 14. This probability is much lower the failure rate of other hardware components, for example, the hard-disk drive.
And by adjusting the value of p, PARA can provide an arbitrarily strong-degree of protection against errors.

## Slide 138: Advantages of PARA
PARA refreshes rows infrequently
  Low power
  Low performance-overhead
    Average slowdown: 0.20% (for 29 benchmarks)
    Maximum slowdown: 0.75%
PARA is stateless
  Low cost
  Low complexity
PARA is an effective and low-overhead solution to prevent disturbance errors
Notes: PARA has many advantages. Since it refreshes row infrequently, it has low power and low performance-overhead. Simulated across 29 benchmarks, we saw an average of only 0.2% slowdown and a maximum of only 0.75% slowdown.
In addition, due to its stateless nature, PARA has low cost and complexity.
Therefore, PARA is an effective and low-overhead solution to prevent disturbance errors.

## Slide 139: Requirements for PARA
If implemented in DRAM chip (done today)
  Enough slack in timing and refresh parameters
  Plenty of slack today:
    Lee et al., “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common Case,” HPCA 2015.
    Chang et al., “Understanding Latency Variation in Modern DRAM Chips,” SIGMETRICS 2016.
    Lee et al., “Design-Induced Latency Variation in Modern DRAM Chips,” SIGMETRICS 2017.
    Chang et al., “Understanding Reduced-Voltage Operation in Modern DRAM Devices,” SIGMETRICS 2017.
    Ghose et al., “What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study,” SIGMETRICS 2018.
    Kim et al., “Solar-DRAM: Reducing DRAM Access Latency by Exploiting the Variation in Local Bitlines,” ICCD 2018.
If implemented in memory controller (done today)
  Better coordination between memory controller and DRAM
  Memory controller should know which rows are physically adjacent

## Slide 140: Probabilistic Activation in Real Life (I)
https://twitter.com/isislovecruft/status/1021939922754723841

## Slide 141: Probabilistic Activation in Real Life (II)
https://twitter.com/isislovecruft/status/1021939922754723841

## Slide 142: First RowHammer Analysis
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data] [Lecture Video (1 hr 49 mins), 25 September 2020] One of the 7 papers of 2012-2017 selected as Top Picks in Hardware and Embedded Security for IEEE TCAD (link).

## Slide 143: Retrospective on RowHammer & Future
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 144: A More Recent RowHammer Retrospective
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version] [Slides from COSADE 2019 (pptx)] [Slides from VLSI-SOC 2020 (pptx) (pdf)] [Talk Video (1 hr 15 minutes, with Q&A)]

## Slide 145: RowHammer in 2020

## Slide 146: RowHammer in 2020 (I)
Jeremie S. Kim, Minesh Patel, A. Giray Yaglikci, Hasan Hassan, Roknoddin Azizi, Lois Orosa, and Onur Mutlu, "Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques" Proceedings of the 47th International Symposium on Computer Architecture (ISCA), Valencia, Spain, June 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 147: Key Takeaways from 1580 Chips
Newer DRAM chips are more vulnerable to RowHammer
There are chips today whose weakest cells fail after only 4800 hammers
Chips of newer DRAM technology nodes can exhibit RowHammer bit flips 1) in more rows and 2) farther away from the victim row.
Existing mitigation mechanisms are NOT effective
Notes: To reiterate our three key takeaways from our experimental characterization, we find that
[CLICK] First, chips of newer DRAM technology nodes are more vulnerable to RowHammer
[CLICK] Second, there are chips today whose weakest cells fail after only 4800 hammers
[CLICK] Third, chips of newer DRAM technology nodes can exhibit RowHammer bit flips in more rows and farther away from the victim row
================

## Slide 148: RowHammer in 2020 (II)
Pietro Frigo, Emanuele Vannacci, Hasan Hassan, Victor van der Veen, Onur Mutlu, Cristiano Giuffrida, Herbert Bos, and Kaveh Razavi, "TRRespass: Exploiting the Many Sides of Target Row Refresh" Proceedings of the 41st IEEE Symposium on Security and Privacy (S&P), San Francisco, CA, USA, May 2020. [Slides (pptx) (pdf)] [Lecture Slides (pptx) (pdf)] [Talk Video (17 minutes)] [Lecture Video (59 minutes)] [Source Code] [Web Article] Best paper award. Pwnie Award 2020 for Most Innovative Research. Pwnie Awards 2020

## Slide 149: TRRespass Key Takeaways
RowHammer is still
an open problem
Security by obscurity
is likely not a good solution

## Slide 150: RowHammer in 2020 (III)
Lucian Cojocar, Jeremie Kim, Minesh Patel, Lillian Tsai, Stefan Saroiu, Alec Wolman, and Onur Mutlu, "Are We Susceptible to Rowhammer? An End-to-End Methodology for Cloud Providers" Proceedings of the 41st IEEE Symposium on Security and Privacy (S&P), San Francisco, CA, USA, May 2020. [Slides (pptx) (pdf)] [Talk Video (17 minutes)]

## Slide 151: RowHammer in 2020 (IV)

## Slide 152: RowHammer in 2020 (V)

## Slide 153: RowHammer in 2020 (VI)

## Slide 154: BlockHammer Solution in 2021
A. Giray Yaglikci, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (22 minutes)] [Short Talk Video (7 minutes)]

## Slide 155: Two Key RowHammer Papers at MICRO 2021
Lois Orosa, Abdullah Giray Yaglikci, Haocong Luo, Ataberk Olgun, Jisung Park, Hasan Hassan, Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [arXiv version]

## Slide 156: Two Key RowHammer Papers at MICRO 2021
Hasan Hassan, Yahya Can Tugrul, Jeremie S. Kim, Victor van der Veen, Kaveh Razavi, and Onur Mutlu, "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [arXiv version]

## Slide 157: More to Come…

## Slide 158: Detailed Lectures on RowHammer
Computer Architecture, Fall 2020, Lecture 4b
  RowHammer (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=KDy632z23UE&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=8
Computer Architecture, Fall 2020, Lecture 5a
  RowHammer in 2020: TRRespass (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=pwRw7QqK_qA&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=9
Computer Architecture, Fall 2020, Lecture 5b
  RowHammer in 2020: Revisiting RowHammer (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=gR7XR-Eepcg&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=10
Computer Architecture, Fall 2020, Lecture 5c
  Secure and Reliable Memory (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=HvswnsfG3oQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=11
https://www.youtube.com/onurmutlulectures

## Slide 159: The Story of RowHammer Lecture …
Onur Mutlu, "The Story of RowHammer" Keynote Talk at Secure Hardware, Architectures, and Operating Systems Workshop (SeHAS), held with HiPEAC 2021 Conference, Virtual, 19 January 2021. [Slides (pptx) (pdf)] [Talk Video (1 hr 15 minutes, with Q&A)]

## Slide 160: Most Recent RowHammer Lecture
https://www.youtube.com/watch?v=7wVKnPj3NVw&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF&index=5

## Slide 161
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 162: Future of Main Memory Reliability
DRAM is becoming less reliable  more vulnerable
Due to difficulties in DRAM scaling, other problems may also appear (or they may be going unnoticed)
Some errors may already be slipping into the field
  Read disturb errors (Rowhammer)
  Retention errors
  Read errors, write errors
  …
These errors can also pose security vulnerabilities

## Slide 163: All Memory Technologies are Vulnerable
DRAM
Flash memory
Emerging Technologies
  Phase Change Memory
  STT-MRAM
  RRAM, memristors
  …

## Slide 164: How Do We Keep Memory Secure?
Understand: Methodologies for failure modeling and discovery
  Modeling and prediction based on real (device) data
Architect: Principled co-architecting of system and memory
  Good partitioning of duties across the stack
Design & Test: Principled design, automation, testing
  High coverage and good interaction with system reliability methods

## Slide 165
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Understand and Model with Experiments (DRAM)

## Slide 166: Understand and Model with Experiments (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017,
PIEEE 2017, HPCA 2018, SIGMETRICS 2018]
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 167: Understanding Flash Memory Reliability
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 168: Lecture on Flash Memory & SSDs
https://www.youtube.com/watch?v=rninK6KWBeM&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=47

## Slide 169: Special Course on Flash Memory & SSDs
https://www.youtube.com/watch?v=dSsZA6JGcLE&list=PL5Q2soXY2Zi_4tPsgX9m_D7AI_c1T86cO

## Slide 170: Challenge and Opportunity for Future
Fundamentally
Secure, Reliable, Safe
Computing Architectures

## Slide 171: One Important Takeaway
Main Memory Needs
Intelligent Controllers

## Slide 172: The Takeaway, Again
In-Field Patch-ability
(Intelligent Memory)
Can Avoid Many Failures

## Slide 173: Four Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency and Predictable Architectures
Architectures for AI/ML, Genomics, Medicine, Health

## Slide 174: Maslow’s (Human) Hierarchy of Needs, Revisited
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Everlasting energy
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.

## Slide 175: Do We Want This?
Source: V. Milutinovic

## Slide 176: Or This?
Source: V. Milutinovic

## Slide 177: Challenge and Opportunity for Future
High Performance,
Energy Efficient,
Sustainable

## Slide 178: The Problem
Data access is the major performance and energy bottleneck
Our current
design principles
cause great energy waste
(and great performance loss)

## Slide 179: The Problem
Processing of data
is performed
far away from the data

## Slide 180: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 181: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 182: Today’s Computing Systems
Are overwhelmingly processor centric
All data processed in the processor  at great system cost
Processor is heavily optimized and is considered the master
Data storage units are dumb and are largely unoptimized (except for some that are on the processor die)

## Slide 183: Yet …
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 184: The Performance Perspective
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors" Proceedings of the 9th International Symposium on High-Performance Computer Architecture (HPCA), pages 129-140, Anaheim, CA, February 2003. Slides (pdf)
  One of the 15 computer arch. papers of 2003 selected as Top Picks by IEEE Micro. HPCA Test of Time Award (awarded in 2021).

## Slide 185: The Performance Perspective (2015)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 186: The Performance Perspective (2015)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 187: Perils of Processor-Centric Design
Grossly-imbalanced systems
  Processing done only in one place
  Everything else just stores and moves data: data moves a lot
   Energy inefficient
   Low performance
   Complex
Overly complex and bloated processor (and accelerators)
  To tolerate data access from memory
  Complex hierarchies and mechanisms
   Energy inefficient
   Low performance
   Complex

## Slide 188: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data
Yet, system is still bottlenecked by memory

## Slide 189: Three Key Systems Trends
1. Data access is a major bottleneck
  Applications are increasingly data hungry
2. Energy consumption is a key limiter
3. Data movement energy dominates compute
  Especially true for off-chip to on-chip movement

## Slide 190: Data Movement vs. Computation Energy
Dally, HiPEAC 2015

## Slide 191: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 192: Data Movement vs. Computation Energy
Data movement is a major system energy bottleneck
  Comprises 41% of mobile system energy during web browsing [2]
  Costs ~115 times as much energy as an ADD operation [1, 2]
[1]: Reducing data Movement Energy via Online Data Clustering and Encoding (MICRO’16)
[2]: Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms (IISWC’14)

## Slide 193: Energy Waste in Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 194: We Do Not Want to Move Data!
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 195: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 196: Goal: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processor chip and in-memory units?
  software and hardware interfaces?
  system software, compilers, languages?
  algorithms and theoretical foundations?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 197: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 200: We Need to Think Differently from the Past Approaches

## Slide 201: Processing in Memory: Two Approaches
1. Processing using Memory
2. Processing near Memory

## Slide 202: Two PIM Approaches
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021. [Tutorial Video on "Memory-Centric Computing Systems" (1 hour 51 minutes)]
https://people.inf.ethz.ch/omutlu/pub/ModernPrimerOnPIM_springer-emerging-computing-bookchapter21.pdf

## Slide 203: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 204: Today’s Systems: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 205: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 206: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 207: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 208: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 209: RowClone Extensions and Follow-Up Work
Can this be improved to do faster inter-subarray copy?
  Yes, see LISA [Chang et al., HPCA 2016]
Can we enable data movement at smaller granularities within a bank?
  Yes, see FIGARO [Wang et al., MICRO 2020]
Can this be improved to do better inter-bank copy?
  Yes, see Network-on-Memory [CAL 2020]
Can similar ideas and DRAM properties be used to perform computation on data?
  Yes, see Ambit [Seshadri et al., CAL 2015, MICRO 2017]

## Slide 210: LISA: Increasing Connectivity in DRAM
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 211: FIGARO: Fine-Grained In-DRAM Copy
Yaohua Wang, Lois Orosa, Xiangjun Peng, Yang Guo, Saugata Ghose, Minesh Patel, Jeremie S. Kim, Juan Gómez Luna, Mohammad Sadrosadati, Nika Mansouri Ghiasi, and Onur Mutlu, "FIGARO: Improving System Performance via Fine-Grained In-DRAM Data Relocation and Caching" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020.

## Slide 212: Network-On-Memory: Fast Inter-Bank Copy
Seyyed Hossein SeyyedAghaei Rezaei, Mehdi Modarressi, Rachata Ausavarungnirun, Mohammad Sadrosadati, Onur Mutlu, and Masoud Daneshtalab, "NoM: Network-on-Memory for Inter-Bank Data Transfer in Highly-Banked Memories" IEEE Computer Architecture Letters (CAL), to appear in 2020.

## Slide 213: Mindset: Memory as an Accelerator
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 214: In-Memory Bulk Bitwise Operations
We can also support in-DRAM AND, OR, NOT, MAJ
At low cost
Using analog computation capability of DRAM
  Idea: activating multiple rows performs computation
30-60X performance and energy improvement
  Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
New memory technologies enable even more opportunities
  Memristors, resistive RAM, phase change mem, STT-MRAM, …
  Can operate on data with minimal movement

## Slide 215: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 216: In-DRAM Acceleration of Database Queries
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 217: More on In-DRAM Bulk AND/OR
Vivek Seshadri, Kevin Hsieh, Amirali Boroumand, Donghyuk Lee, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Fast Bulk Bitwise AND and OR in DRAM" IEEE Computer Architecture Letters (CAL), April 2015.

## Slide 218: More on Ambit
Vivek Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.

## Slide 219: In-DRAM Bulk Bitwise Execution
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]

## Slide 220: SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 221: SIMDRAM Key Idea
SIMDRAM: An end-to-end processing-using-DRAM framework that provides the programming interface, the ISA, and the hardware support for:
  Efficiently computing complex operations in DRAM
  Providing the ability to implement arbitrary operations as required
  Using an in-DRAM massively-parallel SIMD substrate that requires minimal changes to DRAM architecture
23

## Slide 222: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
27
New SIMDRAM Program
Program

## Slide 223: More on the SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 224: In-DRAM Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 225: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 226: Processing in Memory: Two Approaches
1. Processing using Memory
2. Processing near Memory

## Slide 227: Another Example: In-Memory Graph Processing
Large graphs are everywhere (circa 2015)
Scalable large-scale graph processing is challenging
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos
Chart: Speedup
| 128 Cores | 32 Cores
열3 | 1.4206 | 1

## Slide 228: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 229: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 230: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 231: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communications via Remote Function Calls

## Slide 232: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 233: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
Tesseract
32 Tesseract Cores
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 234: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
On five graph processing algorithms

## Slide 235: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
Chart: Memory Bandwidth Consumption
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 0.079545 | 0.1904 | 0.24289 | 1.2943 | 2.244 | 2.9197

## Slide 236: Tesseract Graph Processing System Energy
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
> 8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 237: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 238: PIM on Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.

## Slide 239: Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Amirali Boroumand
Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun,
Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu

## Slide 240: Consumer Devices
Consumer devices are everywhere!
Energy consumption is a first-class concern in consumer devices
Notes: Consumer devices like tablets smartphone and wearable are now everywhere and used by billions of people.
One of the major challenge in these devices is battery limitation which makes the energy consumption a critical concern …

## Slide 241: Four Important Workloads
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 242: Energy Cost of Data Movement
Data Movement
1st key observation: 62.7% of the total system energy is spent on data movement
  Potential solution: move computation close to data
  Challenge: limited area and energy budget
Processing-In-Memory (PIM)
SoC
DRAM
L2
L1
CPU
CPU
CPU
CPU
Compute Unit
Notes: Throughout our analysis, we make a key observation that out of all sources of energy consumption, data movement is a major contributor to the total system energy. We find that across all of the workloads, on average around 62.7% of total system energy is spent on data movement.
One way to reduce data movement cost is to move computation close to data, or …
One potential solution to address this cost it do move computation close to data, or in other words, do procesing in memory. However, the challenge is that these devices.
One potential solution to mitigate data movement cost and reduce total system energy is to execute data-movement heavy portions of application close to data, or in other words, do processing in memory. However, consumer devices are extermely limited in terms of area and power budget. So the question is can we move part of the data movement heavy portion given the limited area and energy budget. Our

## Slide 243: Using PIM to Reduce Data Movement
  2nd key observation: a significant fraction of the data movement often comes from simple functions
PIM Core
PIM Accelerator
PIM Accelerator
PIM Accelerator
We can design lightweight logic to implement these simple functions in memory
Small embedded low-power core
Small fixed-function accelerators
  Offloading to PIM logic reduces energy and improves performance, on average, by 2.3X and 2.2X
Notes: To figure out if we can use processing in memory, we dig deeper into our analysis and we make another key observation that majority of data movement often comes form simple functions and pritmitives. We find that these simple function can be implemented in memory as either a small embedded core, or group of small fixed function accelerators. Our result shows that offloading these function to PIM logic can significantly reduce data movement for each function and reduce energy on average around 55% and improve perforamcne around 54%.
our PIM core can reduce significant portion of data movement, reduce enregy by 49.1% for each function and improve performance up to 2.2X. While using group of fixed function accelerator reduce energy by 55.4% and improve performance by up to 2.5X.
  Or use Saugata’s approach : Reduces total system energy by an average of 55.4%
  Reduces execution time by an average of 54.2%
Our result show that both of them can significantly reduce the data movement for each function.
Feedback: talk about result more
Don’t talk about specific detail like MemCopy, MemSet stuff like that
Main take away: data movement come from simple functions that are simple enough to implement in PIM
We find that these functions and primitves can be implemented as PIM logic using either (1) a small low-power general-purpose embedded core or (2) a group of small fixed-function accelerators (PIM accelerators). Our Analysis shows that both are cost-feasible to use in consumer devices. We find that they eliminate a significant fraction of dat amovement, and reduce energy consumption for each of these operation on average by 49 and 55%.

## Slide 244: Workload Analysis
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 245: TensorFlow Mobile
57.3% of the inference energy is spent on data movement
54.4% of the data movement energy comes from packing/unpacking and quantization
Inference
Prediction

## Slide 246: More on PIM for Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Lightning Talk Video (2 minutes)] [Full Talk Video (21 minutes)]

## Slide 247: Truly Distributed GPU Processing with PIM
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
SM (Streaming Multiprocessor)

## Slide 248: Accelerating GPU Execution with PIM (I)
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 249: Accelerating GPU Execution with PIM (II)
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 250: Accelerating Linked Data Structures
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 251: Accelerating Dependent Cache Misses
Milad Hashemi, Khubaib, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "Accelerating Dependent Cache Misses with an Enhanced Memory Controller" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 252: Accelerating Runahead Execution
Milad Hashemi, Onur Mutlu, and Yale N. Patt, "Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads" Proceedings of the 49th International Symposium on Microarchitecture (MICRO), Taipei, Taiwan, October 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pdf)] [Poster (pptx) (pdf)]

## Slide 253: Accelerating Climate Modeling
Gagandeep Singh, Dionysios Diamantopoulos, Christoph Hagleitner, Juan Gómez-Luna, Sander Stuijk, Onur Mutlu, and Henk Corporaal, "NERO: A Near High-Bandwidth Memory Stencil Accelerator for Weather Prediction Modeling" Proceedings of the 30th International Conference on Field-Programmable Logic and Applications (FPL), Gothenburg, Sweden, September 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (23 minutes)] Nominated for the Stamatis Vassiliadis Memorial Award.

## Slide 254: Accelerating Approximate String Matching
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 255: Accelerating Time Series Analysis
Ivan Fernandez, Ricardo Quislant, Christina Giannoula, Mohammed Alser, Juan Gómez-Luna, Eladio Gutiérrez, Oscar Plata, and Onur Mutlu, "NATSA: A Near-Data Processing Accelerator for Time Series Analysis" Proceedings of the 38th IEEE International Conference on Computer Design (ICCD), Virtual, October 2020. [Slides (pptx) (pdf)] [Talk Video (10 minutes)]

## Slide 256: DAMOV Methodology & Workloads
https://arxiv.org/pdf/2105.03725.pdf

## Slide 257: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 258: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 261: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 262: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 263: UPMEM Memory Modules
E19: 8 chips DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 264: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 265: More on the UPMEM PIM System
https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=26

## Slide 266: Experimental Analysis of the UPMEM PIM Engine
https://arxiv.org/pdf/2105.03814.pdf

## Slide 267: PrIM Benchmarks: Application Domains
Domain | Benchmark | Short name
Dense linear algebra | Vector Addition | VA
 | Matrix-Vector Multiply | GEMV
Sparse linear algebra | Sparse Matrix-Vector Multiply | SpMV
Databases | Select | SEL
 | Unique | UNI
Data analytics | Binary Search | BS
 | Time Series Analysis | TS
Graph processing | Breadth-First Search | BFS
Neural networks | Multilayer Perceptron | MLP
Bioinformatics | Needleman-Wunsch | NW
Image processing | Image histogram (short) | HST-S
 | Image histogram (large) | HST-L
Parallel primitives | Reduction | RED
 | Prefix sum (scan-scan-add) | SCAN-SSA
 | Prefix sum (reduce-scan-scan) | SCAN-RSS
 | Matrix transposition | TRNS

## Slide 268: PrIM Benchmarks are Open Source
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 269: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 270: Understanding a Modern PIM Architecture
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 271: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 272: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=Pp9jSU2b9oM&list=PL5Q2soXY2Zi8_VVChACnON4sfh2bJ5IrD&index=159

## Slide 273: FPGA-based Processing Near Memory
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), to appear, 2021.

## Slide 274: DAMOV Analysis Methodology & Workloads
https://arxiv.org/pdf/2105.03725.pdf

## Slide 275: Step 1: Application Profiling
We analyze 345 applications from distinct domains:
25
Graph Processing
Deep Neural Networks
Physics
High-Performance Computing
Genomics
Machine Learning
Databases
Data Reorganization
Image Processing
Map-Reduce
Benchmarking
Linear Algebra
…
Physics
Security
Machine learning
Database
Graph processing
Data analytics
Data reorganization
Genomics
Deep Neural Networks
Image processing
Linear algebra
Signal processing
Data mining
Notes: In this work, we analyzed 345 applications from distinct domains, from
[CLICK] GRAPH Processing [CLICK] Neural Networks
[CLICK] Physics [CLICK] High-performance computing
[CLICK]Genomics [CLICK] And more
[NEXT]

## Slide 276: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
44
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 277: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
44
Get DAMOV at:
https://github.com/CMU-SAFARI/DAMOV
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 278: More on DAMOV Analysis Methodology & Workloads
https://www.youtube.com/watch?v=GWideVyo0nM&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9&index=3

## Slide 279: More on DAMOV
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" Preprint in arXiv, 8 May 2021. [arXiv preprint] [DAMOV Suite and Simulator Source Code] [SAFARI Live Seminar Video (2 hrs 40 mins)] [Short Talk Video (21 minutes)]

## Slide 280: Samsung Function-in-Memory DRAM (2021)
https://news.samsung.com/global/samsung-develops-industrys-first-high-bandwidth-memory-with-ai-processing-power

## Slide 281: Samsung Function-in-Memory DRAM (2021)

## Slide 282: Samsung Function-in-Memory DRAM (2021)

## Slide 283: Detailed Lectures on PIM (I)
Computer Architecture, Fall 2020, Lecture 6
  Computation in Memory (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=oGcZAGwfEUE&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=12
Computer Architecture, Fall 2020, Lecture 7
  Near-Data Processing (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=j2GIigqn1Qw&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=13
Computer Architecture, Fall 2020, Lecture 11a
  Memory Controllers (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=TeG773OgiMQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=20
Computer Architecture, Fall 2020, Lecture 12d
  Real Processing-in-DRAM with UPMEM (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=25
https://www.youtube.com/onurmutlulectures

## Slide 284: Detailed Lectures on PIM (II)
Computer Architecture, Fall 2020, Lecture 15
  Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=AlE1rD9G_YU&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=28
Computer Architecture, Fall 2020, Lecture 16a
  Opportunities & Challenges of Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=pmLszWGmMGQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=29
Computer Architecture, Fall 2020, Guest Lecture
  In-Memory Computing: Memory Devices & Applications (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=wNmqQHiEZNk&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=41
https://www.youtube.com/onurmutlulectures

## Slide 285: A Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 286: A Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 287: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 288: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 289: Challenge and Opportunity for Future
Fundamentally
High-Performance
(Data-Centric)
Computing Architectures

## Slide 290: Four Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency and Predictable Architectures
Architectures for AI/ML, Genomics, Medicine, Health

## Slide 291: Concluding Remarks

## Slide 292: A Quote from A Famous Architect
“architecture […] based upon principle, and not upon precedent”

## Slide 293: Precedent-Based Design
“architecture […] based upon principle, and not upon precedent”

## Slide 294: Principled Design
“architecture […] based upon principle, and not upon precedent”

## Slide 296: Another Example: Precedent-Based Design
Source: http://cookiemagik.deviantart.com/art/Train-station-207266944

## Slide 297: Principled Design
Source: By Toni_V, CC BY-SA 2.0, https://commons.wikimedia.org/w/index.php?curid=4087256

## Slide 298: Another Principled Design
Source: By Martín Gómez Tagle - Lisbon, Portugal, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=13764903
Source: http://www.arcspace.com/exhibitions/unsorted/santiago-calatrava/

## Slide 299: Another Principled Design
Source: CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=172107

## Slide 300: Principle Applied to Another Structure
Source: https://www.dezeen.com/2016/08/29/santiago-calatrava-oculus-world-trade-center-transportation-hub-new-york-photographs-hufton-crow/
Source: By 準建築人手札網站 Forgemind ArchiMedia - Flickr: IMG_2489.JPG, CC BY 2.0,
https://commons.wikimedia.org/w/index.php?curid=31493356, https://en.wikipedia.org/wiki/Santiago_Calatrava

## Slide 301: Overarching Principles for Computing?
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 302: Fundamentally Better Architectures
Data-centric
Data-driven
Data-aware

## Slide 303: A Blueprint for Fundamentally Better Architectures
Onur Mutlu, "Intelligent Architectures for Intelligent Computing Systems" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Virtual, February 2021. [Slides (pptx) (pdf)] [IEDM Tutorial Slides (pptx) (pdf)] [Short DATE Talk Video (11 minutes)] [Longer IEDM Tutorial Video (1 hr 51 minutes)]

## Slide 304: We Need to Exploit Good Principles
Data-centric design
All components intelligent
Good cross-layer communication, expressive interfaces
Better-than-worst-case design
Heterogeneity
Flexibility, adaptability
Open minds

## Slide 305: Concluding Remarks
It is time to design principled computing architectures to achieve the highest security, performance, and efficiency
Discover design principles for fundamentally secure and reliable computer architectures
Design complete systems to be balanced and energy-efficient, i.e., data-centric (or memory-centric) and low-latency
Enable new platforms for genomics, medicine, health, AI/ML
This can
  Lead to orders-of-magnitude improvements
  Enable new applications & computing platforms
  Enable better understanding of nature
  …
Notes: Perhaps we have taken processor-centric system design a bit too far

## Slide 306: The Future is Very Bright
Regardless of challenges
  in underlying technology and overlying problems/requirements
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 307: We Need to Think and Act Across the Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 308: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 311: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 312: A Tutorial on Memory-Centric Systems
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 314: Funding Acknowledgments
Alibaba, AMD, ASML, Google, Facebook, Hi-Silicon, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware
NSF
NIH
GSRC
SRC
CyLab

## Slide 315: Acknowledgments
My current and past students and postdocs
  Rachata Ausavarungnirun, Abhishek Bhowmick, Amirali Boroumand, Rui Cai, Yu Cai, Kevin Chang, Saugata Ghose, Kevin Hsieh, Tyler Huberty, Ben Jaiyen, Samira Khan, Jeremie Kim, Yoongu Kim, Yang Li, Jamie Liu, Lavanya Subramanian, Donghyuk Lee, Yixin Luo, Justin Meza, Gennady Pekhimenko, Vivek Seshadri, Lavanya Subramanian, Nandita Vijaykumar, HanBin Yoon, Jishen Zhao, …
My collaborators
  Can Alkan, Chita Das, Phil Gibbons, Sriram Govindan, Norm Jouppi, Mahmut Kandemir, Mike Kozuch, Konrad Lai, Ken Mai, Todd Mowry, Yale Patt, Moinuddin Qureshi, Partha Ranganathan, Bikash Sharma, Kushagra Vaid, Chris Wilkerson, …

## Slide 316: Acknowledgments
Think BIG, Aim HIGH!
https://safari.ethz.ch

## Slide 317
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 318: SAFARI Newsletter April 2020 Edition
https://safari.ethz.ch/safari-newsletter-april-2020/

## Slide 319: SAFARI Newsletter January 2021 Edition
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 320: Future Computing Platforms Challenges and Opportunities
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
10 November 2021
EdukCircle Intl. Conv. on Engineering & Computer Technology

## Slide 321: Four Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency and Predictable Architectures
Architectures for AI/ML, Genomics, Medicine, Health

## Slide 322: Low Latency Communication is Critical
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 323: Maslow’s Hierarchy of Needs, A Third Time
Speed
Speed
Speed
Speed
Speed
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.

## Slide 324: Challenge and Opportunity for Future
Fundamentally
Low-Latency
Computing Architectures

## Slide 325: Main Memory Latency Lags Behind
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 326: The Memory Latency Problem
High memory latency is a significant limiter of system performance and energy-efficiency
It is becoming increasingly so with higher memory contention in multi-core and heterogeneous architectures
  Exacerbating the bandwidth need
  Exacerbating the QoS problem
It increases processor design complexity due to the mechanisms incorporated to tolerate memory latency

## Slide 327: Retrospective: Conventional Latency Tolerance Techniques
Caching [initially by Wilkes, 1965]
  Widely used, simple, effective, but inefficient, passive
  Not all applications/phases exhibit temporal or spatial locality
Prefetching [initially in IBM 360/91, 1967]
  Works well for regular memory access patterns
  Prefetching irregular access patterns is difficult, inaccurate, and hardware-intensive
Multithreading [initially in CDC 6600, 1964]
  Works well if there are multiple threads
  Improving single thread performance using multithreading hardware is an ongoing research effort
Out-of-order execution [initially by Tomasulo, 1967]
  Tolerates cache misses that cannot be prefetched
  Requires extensive hardware resources for tolerating long latencies
None of These
Fundamentally Reduce
Memory Latency

## Slide 328: Truly Reducing Memory Latency

## Slide 329: Why the Long Memory Latency?
Reason 1: Design of DRAM Micro-architecture
  Goal: Maximize capacity/area, not minimize latency
Reason 2: “One size fits all” approach to latency specification
  Same latency parameters for all temperatures
  Same latency parameters for all DRAM chips
  Same latency parameters for all parts of a DRAM chip
  Same latency parameters for all supply voltage levels
  Same latency parameters for all application data
  …

## Slide 330: Tackling the Fixed Latency Mindset
Reliable operation latency is actually very heterogeneous
  Across temperatures, chips, parts of a chip, voltage levels, …
Idea: Dynamically find out and use the lowest latency one can reliably access a memory location with
  Adaptive-Latency DRAM [HPCA 2015]
  Flexible-Latency DRAM [SIGMETRICS 2016]
  Design-Induced Variation-Aware DRAM [SIGMETRICS 2017]
  Voltron [SIGMETRICS 2017]
  DRAM Latency PUF [HPCA 2018]
  DRAM Latency True Random Number Generator [HPCA 2019]
  ...
We would like to find sources of latency heterogeneity and exploit them to minimize latency

## Slide 331: Latency Variation in Memory Chips
High
Low
DRAM Latency
DRAM B
DRAM A
DRAM C
Slow cells
Heterogeneous manufacturing & operating conditions → latency variation in timing parameters

## Slide 332: Why is Latency High?
DRAM latency: Delay as specified in DRAM standards
  Doesn’t reflect true DRAM device latency
Imperfect manufacturing process → latency variation
High standard latency chosen to increase yield
High
Low
DRAM Latency
DRAM A
DRAM B
DRAM C
Manufacturing Variation
Standard
Latency
Notes: To understand the latency problem, we need to go into what defines latency.
DRAM latency is the total amnt of time that the underlying hw operations need <> to retrieve data.
The DRAM standards define a single fixed time for how long these ops should take in every DRAM chip.
However, this defined delay doesn’t actually reflect the latency of the individual DRAMs.
<Timeline illustration>
Because the manufacturing process is imperfect, it introduces variation in the production chips, resulting in latency variation across different chips.
This simple illustartion shows the difference b/w the average latency across 3 different dram chips, to convey the point of latency variation.
It’s important to note that not only does latency variation exists <across> chips, but also <inside> each dram chip itself.
<Blue standard>
Since we don’t want to throw away the chips with high variation, we tolerate them.
The simple way is to <slow> down the acceptable latency so that the majority of chips can all work reliably under this high standard latency.
as we can see, the high standard latency is a result of a trade-off made for higher DRAM production yield.
---
<> Operative word

## Slide 333: What Causes the Long Memory Latency?
Conservative timing margins!
DRAM timing parameters are set to cover the worst case
Worst-case temperatures
  85 degrees vs. common-case
  to enable a wide range of operating conditions
Worst-case devices
  DRAM cell with smallest charge across any acceptable device
  to tolerate process variation at acceptable yield
This leads to large timing margins for the common case

## Slide 334: Understanding and Exploiting Variation in DRAM Latency

## Slide 335: DRAM Characterization Infrastructure
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 336: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer provides multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 337
Latency Reduction Summary of 115 DIMMs
Latency reduction for read & write (55°C)
  Read Latency: 32.7%
  Write Latency: 55.1%
Latency reduction for each timing parameter (55°C)
  Sensing: 17.3%
  Restore: 37.3% (read), 54.8% (write)
  Precharge: 35.2%
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 338
AL-DRAM: Real System Evaluation
System
  CPU: AMD 4386 ( 8 Cores, 3.1GHz, 8MB LLC)
  DRAM: 4GByte DDR3-1600 (800Mhz Clock)
  OS: Linux
  Storage: 128GByte SSD
Workload
  35 applications from SPEC, STREAM, Parsec, Memcached, Apache, GUPS

## Slide 339
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
1.4%
6.7%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
5.0%
AL-DRAM: Single-Core Evaluation
AL-DRAM improves single-core performance
on a real system
Performance Improvement
Average
Improvement
all-35-workload

## Slide 340
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
AL-DRAM: Multi-Core Evaluation
AL-DRAM provides higher performance on
multi-programmed & multi-threaded workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 341: Reducing Latency Also Reduces Energy
AL-DRAM reduces DRAM power consumption by 5.8%
Major reason: reduction in row activation time

## Slide 342: More on Adaptive-Latency DRAM
Donghyuk Lee, Yoongu Kim, Gennady Pekhimenko, Samira Khan, Vivek Seshadri, Kevin Chang, and Onur Mutlu, "Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)] [Full data sets]

## Slide 343: CLR-DRAM: Capacity-Latency Reconfigurability
Haocong Luo, Taha Shahroodi, Hasan Hassan, Minesh Patel, A. Giray Yaglikci, Lois Orosa, Jisung Park, and Onur Mutlu, "CLR-DRAM: A Low-Cost DRAM Architecture Enabling Dynamic Capacity-Latency Trade-Off" Proceedings of the 47th International Symposium on Computer Architecture (ISCA), Valencia, Spain, June 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 344: Analysis of Latency Variation in DRAM Chips
Kevin Chang, Abhijith Kashyap, Hasan Hassan, Samira Khan, Kevin Hsieh, Donghyuk Lee, Saugata Ghose, Gennady Pekhimenko, Tianshi Li, and Onur Mutlu, "Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Antibes Juan-Les-Pins, France, June 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 345: Design-Induced Latency Variation in DRAM
Donghyuk Lee, Samira Khan, Lavanya Subramanian, Saugata Ghose, Rachata Ausavarungnirun, Gennady Pekhimenko, Vivek Seshadri, and Onur Mutlu, "Design-Induced Latency Variation in Modern DRAM Chips: Characterization, Analysis, and Latency Reduction Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 346: Solar-DRAM: Putting It Together
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "Solar-DRAM: Reducing DRAM Access Latency by Exploiting the Variation in Local Bitlines" Proceedings of the 36th IEEE International Conference on Computer Design (ICCD), Orlando, FL, USA, October 2018. [Slides (pptx) (pdf)] [Talk Video (16 minutes)]

## Slide 347: Challenge and Opportunity for Future
Fundamentally
Low-Latency
Computing Architectures

## Slide 348: D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput
Jeremie S. Kim Minesh Patel
Hasan Hassan Lois Orosa Onur Mutlu

## Slide 349: DRAM Latency Characterization of 282 LPDDR4 DRAM Devices
Latency failures come from accessing DRAM with reduced timing parameters.
Key Observations:
  A cell’s latency failure probability is determined by random process variation
  Some cells fail randomly
Notes: In this work, we show results from a detailed experimental characterization of 282 state-of-the-art LPDDR4 DRAM devices. [CLICK] We characterize DRAM latency by observing the effects of accessing DRAM with DRAM timing parameters reduced below manufacturer-recommended values.
[CLICK] We make two key observations. [CLICK] first, a cell’s probability to fail, when accessed with reduced timing parameters, is directly correlated with random variations that arise from process manufacturing. [CLICK] secondly, We note that some cells fail randomly when accessed with a reduced tRCD.

## Slide 350: D-RaNGe Key Idea
Row Decoder
High % chance to fail with reduced tRCD
Low % chance to fail with reduced tRCD
SA
SA
SA
SA
SA
SA
SA
Fails randomly
with reduced tRCD
Notes: Here is a cartoon showing the manufacturing variation across a region of DRAM. When accessed with a reduced timing parameter, [CLICK] some cells have a high percentage chance of failing, while others [CLICK] have a low percentage chance of failing. [CLICK} Some cells fail randomly when accessed with a reduced tRCD.

## Slide 351: D-RaNGe Key Idea
Row Decoder
High % chance to fail with reduced tRCD
Low % chance to fail with reduced tRCD
SA
SA
SA
SA
SA
SA
SA
Fails randomly
with reduced tRCD
We refer to cells that fail randomly
when accessed with a reduced tRCD
as RNG cells
Notes: We refer to cells that fail randomly when accessed with a reduced tRCD as RNG cells

## Slide 352: Our D-RaNGe Evaluation
We generate random values by repeatedly accessing RNG cells and aggregating the data read
The random data satisfies the NIST statistical test suite for randomness
The D-RaNGE generates random numbers
  Throughput: 717.4 Mb/s
  Latency: 64 bits in <1us
  Power: 4.4 nJ/bit

## Slide 353: DRAM Latency True Random Number Generator
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 354: DRAM Latency Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 355: Lectures on Low-Latency Memory
Computer Architecture, Fall 2020, Lecture 10
  Low-Latency Memory (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=vQd1YgOH1Mw&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=19
Computer Architecture, Fall 2020, Lecture 12b
  Capacity-Latency Reconfigurable DRAM (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=DUtPFW3jxq4&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=23
Computer Architecture, Fall 2019, Lecture 11a
  DRAM Latency PUF (ETH Zürich, Fall 2019)
  https://www.youtube.com/watch?v=7gqnrTZpjxE&list=PL5Q2soXY2Zi-DyoI3HbqcdtUm9YWRR_z-&index=15
Computer Architecture, Fall 2019, Lecture 11b
  DRAM True Random Number Generator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=Y3hPv1I5f8Y&list=PL5Q2soXY2Zi-DyoI3HbqcdtUm9YWRR_z-&index=16
https://www.youtube.com/onurmutlulectures

## Slide 356: A Tutorial on Low-Latency Memory
https://www.youtube.com/onurmutlulectures

## Slide 357: Challenge and Opportunity for Future
Fundamentally
Low-Latency
Computing Architectures

## Slide 358: Four Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency and Predictable Architectures
Architectures for AI/ML, Genomics, Medicine, Health

## Slide 359: Intel Optane Persistent Memory (2019)
Non-volatile main memory
Based on 3D-XPoint Technology
https://www.storagereview.com/intel_optane_dc_persistent_memory_module_pmm

## Slide 360: PCM as Main Memory: Idea in 2009
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)

## Slide 361: PCM as Main Memory: Idea in 2009
Benjamin C. Lee, Ping Zhou, Jun Yang, Youtao Zhang, Bo Zhao, Engin Ipek, Onur Mutlu, and Doug Burger, "Phase Change Technology and the Future of Main Memory" IEEE Micro, Special Issue: Micro's Top Picks from 2009 Computer Architecture Conferences (MICRO TOP PICKS), Vol. 30, No. 1, pages 60-70, January/February 2010.

## Slide 362: Cerebras’s Wafer Scale Engine (2019)
Cerebras WSE
1.2 Trillion transistors
46,225 mm2
Largest GPU
21.1 Billion transistors
815 mm2
The largest ML
accelerator chip
400,000 cores
NVIDIA TITAN V
https://www.anandtech.com/show/14758/hot-chips-31-live-blogs-cerebras-wafer-scale-deep-learning
https://www.cerebras.net/cerebras-wafer-scale-engine-why-we-need-big-chips-for-deep-learning/
Notes: The Wafer-Scale Engine is the most massive AI chip ever produced and packs a whopping 400,000 cores in a 46,225mm2 footprint.

## Slide 363: Cerebras’s Wafer Scale Engine-2 (2021)
Cerebras WSE-2
2.6 Trillion transistors
46,225 mm2
Largest GPU
54.2 Billion transistors
826 mm2
The largest ML
accelerator chip (2021)
850,000 cores
NVIDIA Ampere GA100
https://www.anandtech.com/show/14758/hot-chips-31-live-blogs-cerebras-wafer-scale-deep-learning
https://www.cerebras.net/cerebras-wafer-scale-engine-why-we-need-big-chips-for-deep-learning/

## Slide 364: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 365: Experimental Analysis of the UPMEM PIM Engine
https://arxiv.org/pdf/2105.03814.pdf

## Slide 366: Samsung Function-in-Memory DRAM (2021)
https://news.samsung.com/global/samsung-develops-industrys-first-high-bandwidth-memory-with-ai-processing-power

## Slide 367: Samsung Function-in-Memory DRAM (2021)

## Slide 368: Samsung Function-in-Memory DRAM (2021)

## Slide 369: Samsung Function-in-Memory DRAM (2021)

## Slide 370: Samsung Function-in-Memory DRAM (2021)

## Slide 371: More on Processing in Memory (I)
Vivek Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.

## Slide 372: More on Processing in Memory (II)
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]

## Slide 373: More on Processing in Memory (III)
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 374: More on Processing in Memory (IV)
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 375: More on Processing in Memory (V)
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.

## Slide 376: More on Processing in Memory (VI)
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 377: TESLA Full Self-Driving Computer (2019)
ML accelerator: 260 mm2, 6 billion transistors, 600 GFLOPS GPU, 12 ARM 2.2 GHz CPUs.
Two redundant chips for better safety.
https://youtu.be/Ucp0TTmvqOE?t=4236

## Slide 378: Google TPU Generation I (~2016)
Jouppi et al., “In-Datacenter Performance Analysis of a Tensor Processing Unit”, ISCA 2017.

## Slide 379: Google TPU Generation II (2017)
https://www.nextplatform.com/2017/05/17/first-depth-look-googles-new-second-generation-tpu/
4 TPU chips
vs 1 chip in TPU1
High Bandwidth Memory
vs DDR3
Floating point operations
vs FP16
45 TFLOPS per chip
vs 23 TOPS
Designed for training
and inference
vs only inference

## Slide 380: Google TPU Generation III
https://cloud.google.com/tpu/docs/system-architecture
32GB HBM per chip
vs 16GB HBM in TPU2
4 Matrix Units per chip
vs 2 Matrix Units in TPU2
90 TFLOPS per chip
vs 45 TFLOPS in TPU2

## Slide 381: An Example Modern Systolic Array: TPU (II)
Jouppi et al., “In-Datacenter Performance Analysis of a Tensor Processing Unit”, ISCA 2017.

## Slide 382: An Example Modern Systolic Array: TPU (III)

## Slide 383: Many (Other) AI/ML Chips
Alibaba
Amazon
Facebook
Google
Huawei
Intel
Microsoft
NVIDIA
Tesla
Many Others and Many Startups…
Many More to Come…

## Slide 384: Many (Other) AI/ML Chips
Alibaba
Amazon
Facebook
Google
Huawei
Microsoft
NVIDIA
Tesla
Many Startups…
Many More to Come…
https://basicmi.github.io/AI-Chip/

## Slide 385: Lectures on Systolic Arrays & ML/AI Acceleration
Digital Design and Computer Architecture, Spring 2021, Lecture 19
  VLIW, Systolic Arrays, DAE (ETH Zürich, Spring 2021)
  https://www.youtube.com/watch?v=UtLy4Yagdys&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN&index=21
Computer Architecture, Fall 2020, Lecture 9b
  EDEN: Efficient DNN Inference (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=HmB32OXMKMY&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=16
Computer Architecture, Fall 2020, Lecture 9c
  SMASH: Accelerating Sparse Matrix Operations (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=78aikMbxkGc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=17
https://www.youtube.com/onurmutlulectures

## Slide 386: Lecture on Systolic Arrays & ML Acceleration
https://www.youtube.com/onurmutlulectures

## Slide 387: Accelerating Genome Analysis

## Slide 388: Our Dream (circa 2007)
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
  Which of these DNAs does this DNA segment match with?
  What is the likely genetic disposition of this patient to this drug?
  What disease/condition might this particular DNA/RNA piece associated with?
  . . .

## Slide 389: What Is a Genome Made Of?
Cell
Nucleus
The discovery of DNA’s double-helical structure (Watson+, 1953)
Notes: Unlocking the life’s code requires diving into the nucleus of our body cells, where the double-stranded genome resides. Genome is literally the 'code of life' - it is the set of instructions for making everything from you to zebras, strawberries, and even yeast.
since the discovery of dna’s double-helical structure (watson et al. 1953)

## Slide 390: DNA Under Electron Microscope
human chromosome #12
from HeLa’s cell
Notes: Henrietta Lacks,

## Slide 391: DNA Sequencing
Goal:
  Find the complete sequence of A, C, G, T’s in DNA.
Challenge:
  There is no machine that takes long DNA as an input, and gives the complete sequence as output
  All sequencing machines chop DNA into pieces and identify relatively small pieces (but not how they fit together)

## Slide 392: Untangling Yarn Balls & DNA Sequencing
Notes: untangling yarn ball

## Slide 393
Genome Sequencers
… and more! All produce data with different properties.
Roche/454
Illumina HiSeq2000
Ion Torrent PGM
Ion Torrent Proton
AB SOLiD
Oxford Nanopore GridION
Oxford Nanopore MinION
Complete
Genomics
Illumina MiSeq
Pacific Biosciences RS
Illumina
NovaSeq
6000

## Slide 394
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 395: Genome Sequence Alignment: Example
Source: By Aaron E. Darling, István Miklós, Mark A. Ragan - Figure 1 from Darling AE, Miklós I, Ragan MA (2008).
"Dynamics of Genome Rearrangement in Bacterial Populations". PLOS Genetics. DOI:10.1371/journal.pgen.1000128., CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=30550950

## Slide 396
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
300 M
bases/min
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Illumina HiSeq4000
2 M
bases/min
on average
(0.6%)
Bottlenecked in Mapping!!
Notes: Typical sequencer machine generates a flood of reads, for example, Illumina HiSeq4000 generates 300 million bases/minute.
However, existing computer alignment algorithms can only process 0.6% of these reads in the same amount of time.
This gap is widening as more advanced sequencers are made available in the market.

## Slide 397: Hash Table Based Read Mappers
+ Guaranteed to find all mappings  sensitive
+ Can tolerate up to e errors
http://mrfast.sourceforge.net/
Alkan+, "Personalized copy number and segmental duplication
maps using next-generation sequencing”, Nature Genetics 2009.
Notes: It turned out the Hash Table based mappers solve the first 2 challenges pretty well. They guarantee to find all mappings with no more than e errors present.

## Slide 398: Read Mapping Execution Time Breakdown
Chart: 
| candidate alignment locations (CAL) | SIMD banded Levenshtein edit distance | SAM printing
Time (sec) | 3738.88 | 81368.0945 | 2269.8755
Notes: An overwhelming majority of the read mapper’s execution time is spent in read alignment.

## Slide 399: Idea
Filter fast before you align
Minimize costly
“approximate string comparisons”

## Slide 400: Our First Filter: Pure Software Approach
Download the source code and try for yourself
  Download link to FastHASH

## Slide 401: Shifted Hamming Distance: SIMD Acceleration
Xin+, "Shifted Hamming Distance: A Fast and Accurate SIMD-friendly Filter
to Accelerate Alignment Verification in Read Mapping”, Bioinformatics 2015.
https://github.com/CMU-SAFARI/Shifted-Hamming-Distance

## Slide 402
GateKeeper: FPGA-Based Alignment Filtering
Alignment Filter
st
1
FPGA-based Alignment Filter.
Notes: To bridge the widening gap between the sequencer & the mapper, we propose the concept of pre-alignment filtering. We added a new examination step before the accurate alignment step. The main objective of this step is to detect the incorrect mappings accurately and rapidly. Only the mappings that pass our filter are examined by the alignment step. We also explore exploiting todays’ hardware accelerators to further boost the filtering speed of such filters.

## Slide 403: GateKeeper: FPGA-Based Alignment Filtering
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 404: DNA Read Mapping & Filtering
Problem: Heavily bottlenecked by Data Movement
GateKeeper FPGA performance limited by DRAM bandwidth [Alser+, Bioinformatics 2017]
Ditto for SHD on SIMD [Xin+, Bioinformatics 2015]
Solution: Processing-in-memory can alleviate the bottleneck
However, we need to design mapping & filtering algorithms to fit processing-in-memory

## Slide 405: In-Memory DNA Sequence Analysis
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" BMC Genomics, 2018. Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. [Slides (pptx) (pdf)] [Source Code] [arxiv.org Version (pdf)] [Talk Video at AACBB 2019]

## Slide 406: Shouji (障子) [Alser+, Bioinformatics 2019]
Mohammed Alser, Hasan Hassan, Akash Kumar, Onur Mutlu, and Can Alkan, "Shouji: A Fast and Efficient Pre-Alignment Filter for Sequence Alignment" Bioinformatics, [published online, March 28], 2019. [Source Code] [Online link at Bioinformatics Journal]

## Slide 407: SneakySnake [Alser+, Bioinformatics 2020]
Mohammed Alser, Taha Shahroodi, Juan-Gomez Luna, Can Alkan, and Onur Mutlu, "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs" Bioinformatics, to appear in 2020. [Source Code] [Online link at Bioinformatics Journal]

## Slide 408: GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 409: Quick Note: Key Principles and Results
Two key principles:
  Exploit the structure of the genome to minimize computation
  Morph and exploit the structure of the underlying hardware to maximize performance and efficiency
Algorithm-architecture co-design for DNA read mapping
  Speeds up read mapping by ~100-1000X
  Improves accuracy of read mapping in the presence of errors

## Slide 410: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION

## Slide 411: Nanopore Genome Assembly Pipeline
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly,” Briefings in Bioinformatics, 2018.

## Slide 412: Recall Our Dream
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
Still a long ways to go
  Energy efficiency
  Performance (latency)
  Security
  Huge memory bottleneck

## Slide 413: Future of Genome Sequencing & Analysis
SmidgION from ONT
MinION from ONT

## Slide 414: Why Do We Care? An Example from 2020
Source: https://nanoporetech.com/about-us/news/200-oxford-nanopore-sequencers-have-left-uk-china-support-rapid-near-sample

## Slide 415: Sequencing of COVID-19
Whole genome sequencing (WGS) and sequence data analysis are important
  To detect the virus from a human sample such as saliva, Bronchoalveolar fluid etc.
  To understand the sources and modes of transmission of the virus
  To discover the genomic characteristics of the virus, and compare with better-known viruses (e.g., 02-03 SARS epidemic)
  To design and evaluate the diagnostic tests and deep-dive studies
Two key areas of COVID-19 genomic research
  To sequence the genome of the virus itself, COVID-19, in order to track the mutations in the virus.
  To explore the genes of infected patients. This analysis can be used to understand why some people get more severe symptoms than others, as well as, help with the development of new treatments in the future.

## Slide 416: COVID-19 Nanopore Sequencing (I)
From ONT (https://nanoporetech.com/covid-19/overview)

## Slide 417: COVID-19 Nanopore Sequencing (II)
From ONT (https://nanoporetech.com/covid-19/overview)

## Slide 418: Future of Genome Sequencing & Analysis
SmidgION from ONT
MinION from ONT

## Slide 419: Accelerating Genome Analysis: Overview
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 420: More on Fast Genome Analysis …
Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" Invited Lecture at Technion, Virtual, 26 January 2021. [Slides (pptx) (pdf)] [Talk Video (1 hour 37 minutes, including Q&A)] [Related Invited Paper (at IEEE Micro, 2020)]

## Slide 421: Detailed Lectures on Genome Analysis
Computer Architecture, Fall 2020, Lecture 3a
  Introduction to Genome Sequence Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=CrRb32v7SJc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=5
Computer Architecture, Fall 2020, Lecture 8
  Intelligent Genome Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=ygmQpdDTL7o&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=14
Computer Architecture, Fall 2020, Lecture 9a
  GenASM: Approx. String Matching Accelerator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=XoLpzmN-Pas&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=15
Accelerating Genomics Project Course, Fall 2020, Lecture 1
  Accelerating Genomics (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=rgjl8ZyLsAg&list=PL5Q2soXY2Zi9E2bBVAgCqLgwiDRQDTyId
https://www.youtube.com/onurmutlulectures

## Slide 422: Challenge and Opportunity for Future
High Performance
(to solve
the toughest & all problems)

## Slide 423: Challenge and Opportunity for Future
Personalized and Private
(in every aspect of life:
health, medicine,
spaces, devices, robotics, …)

## Slide 424: More on My Research & Teaching

## Slide 425: Brief Self Introduction
Onur Mutlu
  Full Professor @ ETH Zurich ITET (INFK), since September 2015
  Strecker Professor @ Carnegie Mellon University ECE/CS, 2009-2016, 2016-…
  PhD from UT-Austin, worked at Google, VMware, Microsoft Research, Intel, AMD
  https://people.inf.ethz.ch/omutlu/
  omutlu@gmail.com (Best way to reach me)
  https://people.inf.ethz.ch/omutlu/projects.htm
Research and Teaching in:
  Computer architecture, computer systems, hardware security, bioinformatics
  Memory and storage systems
  Hardware security, safety, predictability
  Fault tolerance
  Hardware/software cooperation
  Architectures for bioinformatics, health, medicine
  …

## Slide 426: Current Research Mission
Computer architecture, HW/SW, systems, bioinformatics, security
Graphics and Vision Processing
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
Build fundamentally better architectures
Notes: Professor Mutlu’s research focus is all aspects of computer architecture, HW/SW interaction and bioinformatics.
He is looking for students to perform research in these areas.
He and his group, SAFARI, solve fundamental problems spanning:
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
His group does broad research spanning systems to logic with architecture at center

## Slide 427: Four Key Current Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency and Predictable Architectures
Architectures for AI/ML, Genomics, Medicine, Health

## Slide 428: The Transformation Hierarchy
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (narrow view)
Computer Architecture (expanded view)

## Slide 429: Axiom
To achieve the highest energy efficiency and performance:
we must take the expanded view
of computer architecture
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Co-design across the hierarchy:
Algorithms to devices
Specialize as much as possible
within the design goals

## Slide 430: Current Research Mission & Major Topics
Data-centric arch. for low energy & high perf.
  Proc. in Mem/DRAM, NVM, unified mem/storage
Low-latency & predictable architectures
  Low-latency, low-energy yet low-cost memory
  QoS-aware and predictable memory systems
Fundamentally secure/reliable/safe arch.
  Tolerating all bit flips; patchable HW; secure mem
Architectures for ML/AI/Genomics/Health/Med
  Algorithm/arch./logic co-design; full heterogeneity
Data-driven and data-aware architectures
  ML/AI-driven architectural controllers and design
  Expressive memory and expressive systems
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Build fundamentally better architectures
Broad research
spanning apps, systems, logic
with architecture at the center

## Slide 431
38+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-april-2020/

## Slide 432: SAFARI Newsletter January 2021 Edition
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 433: Principle: Teaching and Research
…
Teaching drives Research
Research drives Teaching
…

## Slide 434: Principle: Insight and Ideas
Focus on Insight
Encourage New Ideas

## Slide 435: Research & Teaching: Some Overview Talks
https://www.youtube.com/onurmutlulectures
Future Computing Architectures
  https://www.youtube.com/watch?v=kgiZlSOcGFM&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=1
Enabling In-Memory Computation
  https://www.youtube.com/watch?v=njX_14584Jw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=16
Accelerating Genome Analysis
  https://www.youtube.com/watch?v=r7sn41lH-4A&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=41
Rethinking Memory System Design
  https://www.youtube.com/watch?v=F7xZLNMIY1E&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=3
Intelligent Architectures for Intelligent Machines
  https://www.youtube.com/watch?v=c6_LgzuNdkw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=25
The Story of RowHammer
  https://www.youtube.com/watch?v=sgd7PHQQ1AI&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=39

## Slide 436: An Interview on Research and Education
Computing Research and Education (@ ISCA 2019)
  https://www.youtube.com/watch?v=8ffSEKZhmvo&list=PL5Q2soXY2Zi_4oP9LdL3cc8G6NIjD2Ydz
Maurice Wilkes Award Speech (10 minutes)
  https://www.youtube.com/watch?v=tcQ3zZ3JpuA&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=15

## Slide 437: More Thoughts and Suggestions
Onur Mutlu, "Some Reflections (on DRAM)" Award Speech for ACM SIGARCH Maurice Wilkes Award, at the ISCA Awards Ceremony, Phoenix, AZ, USA, 25 June 2019. [Slides (pptx) (pdf)] [Video of Award Acceptance Speech (Youtube; 10 minutes) (Youku; 13 minutes)] [Video of Interview after Award Acceptance (Youtube; 1 hour 6 minutes) (Youku; 1 hour 6 minutes)] [News Article on "ACM SIGARCH Maurice Wilkes Award goes to Prof. Onur Mutlu"]
Onur Mutlu, "How to Build an Impactful Research Group" 57th Design Automation Conference Early Career Workshop (DAC), Virtual, 19 July 2020. [Slides (pptx) (pdf)]

## Slide 438: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 439: Readings, Videos, Reference Materials

## Slide 440: Research & Teaching: Some Overview Talks
https://www.youtube.com/onurmutlulectures
Future Computing Architectures
  https://www.youtube.com/watch?v=kgiZlSOcGFM&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=1
Enabling In-Memory Computation
  https://www.youtube.com/watch?v=njX_14584Jw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=16
Accelerating Genome Analysis
  https://www.youtube.com/watch?v=r7sn41lH-4A&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=41
Rethinking Memory System Design
  https://www.youtube.com/watch?v=F7xZLNMIY1E&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=3
Intelligent Architectures for Intelligent Machines
  https://www.youtube.com/watch?v=c6_LgzuNdkw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=25
The Story of RowHammer
  https://www.youtube.com/watch?v=sgd7PHQQ1AI&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=39

## Slide 441: Accelerated Memory Course (~6.5 hours)
ACACES 2018
  Memory Systems and Memory-Centric Computing Systems
  Taught by Onur Mutlu July 9-13, 2018
  ~6.5 hours of lectures
Website for the Course including Videos, Slides, Papers
  https://people.inf.ethz.ch/omutlu/acaces2018.html
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi-HXxomthrpDpMJm05P6J9x
All Papers are at:
  https://people.inf.ethz.ch/omutlu/projects.htm
  Final lecture notes and readings (for all topics)

## Slide 442: Longer Memory Course (~18 hours)
TU Wien 2019
  Memory Systems and Memory-Centric Computing Systems
  Taught by Onur Mutlu June 12-19, 2019
  ~18 hours of lectures
Website for the Course including Videos, Slides, Papers
  https://safari.ethz.ch/memory_systems/TUWien2019
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi_gntM55VoMlKlw7YrXOhbl
All Papers are at:
  https://people.inf.ethz.ch/omutlu/projects.htm
  Final lecture notes and readings (for all topics)

## Slide 443: An Interview on Research and Education
Computing Research and Education (@ ISCA 2019)
  https://www.youtube.com/watch?v=8ffSEKZhmvo&list=PL5Q2soXY2Zi_4oP9LdL3cc8G6NIjD2Ydz
Maurice Wilkes Award Speech (10 minutes)
  https://www.youtube.com/watch?v=tcQ3zZ3JpuA&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=15

## Slide 444: More Thoughts and Suggestions
Onur Mutlu, "Some Reflections (on DRAM)" Award Speech for ACM SIGARCH Maurice Wilkes Award, at the ISCA Awards Ceremony, Phoenix, AZ, USA, 25 June 2019. [Slides (pptx) (pdf)] [Video of Award Acceptance Speech (Youtube; 10 minutes) (Youku; 13 minutes)] [Video of Interview after Award Acceptance (Youtube; 1 hour 6 minutes) (Youku; 1 hour 6 minutes)] [News Article on "ACM SIGARCH Maurice Wilkes Award goes to Prof. Onur Mutlu"]
Onur Mutlu, "How to Build an Impactful Research Group" 57th Design Automation Conference Early Career Workshop (DAC), Virtual, 19 July 2020. [Slides (pptx) (pdf)]

## Slide 445: Reference Overview Paper
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 446: Reference Overview Paper I
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "Processing Data Where It Makes Sense: Enabling In-Memory Computation" Invited paper in Microprocessors and Microsystems (MICPRO), June 2019. [arXiv version]
https://arxiv.org/pdf/1903.03988.pdf

## Slide 447: Reference Overview Paper II
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 448: Reference Overview Paper III
Saugata Ghose, Kevin Hsieh, Amirali Boroumand, Rachata Ausavarungnirun, Onur Mutlu, "Enabling the Adoption of Processing-in-Memory: Challenges, Mechanisms, Future Research Directions" Invited Book Chapter, to appear in 2018. [Preliminary arxiv.org version]
https://arxiv.org/pdf/1802.00320.pdf

## Slide 449: Reference Overview Paper IV
Onur Mutlu and Lavanya Subramanian, "Research Problems and Opportunities in Memory Systems" Invited Article in Supercomputing Frontiers and Innovations (SUPERFRI), 2014/2015.
https://people.inf.ethz.ch/omutlu/pub/memory-systems-research_superfri14.pdf

## Slide 450: Reference Overview Paper V
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 451: Reference Overview Paper VI
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Technical talk at MemCon 2013 (MEMCON), Santa Clara, CA, August 2013. [Slides (pptx) (pdf)] [Video] [Coverage on StorageSearch]
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 452: Reference Overview Paper VII
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 453: Reference Overview Paper VIII
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version] [Slides from COSADE 2019 (pptx)] [Slides from VLSI-SOC 2020 (pptx) (pdf)] [Talk Video (30 minutes)]

## Slide 454: Related Videos and Course Materials (I)
Undergraduate Digital Design & Computer Architecture Course Lecture Videos (2020, 2019, 2018, 2017, 2015, 2014, 2013)
Undergraduate Digital Design & Computer Architecture Course Materials (2020, 2019, 2018, 2015, 2014, 2013)
Graduate Computer Architecture Course Lecture Videos (2019, 2018, 2017, 2015, 2013)
Graduate Computer Architecture Course Materials (2019, 2018, 2017, 2015, 2013)
Parallel Computer Architecture Course Materials (Lecture Videos)

## Slide 455: Related Videos and Course Materials (II)
Seminar in Computer Architecture Course Lecture Videos (Spring 2020, Fall 2019, Spring 2019, 2018)
Seminar in Computer Architecture Course Materials (Spring 2020, Fall 2019, Spring 2019, 2018)
Memory Systems Course Lecture Videos (Sept 2019, July 2019, June 2019, October 2018)
Memory Systems Short Course Lecture Materials (Sept 2019, July 2019, June 2019, October 2018)
ACACES Summer School Memory Systems Course Lecture Videos (2018, 2013)
ACACES Summer School Memory Systems Course Materials (2018, 2013)

## Slide 456: Some Open Source Tools (I)
Rowhammer – Program to Induce RowHammer Errors
  https://github.com/CMU-SAFARI/rowhammer
Ramulator – Fast and Extensible DRAM Simulator
  https://github.com/CMU-SAFARI/ramulator
MemSim – Simple Memory Simulator
  https://github.com/CMU-SAFARI/memsim
NOCulator – Flexible Network-on-Chip Simulator
  https://github.com/CMU-SAFARI/NOCulator
SoftMC – FPGA-Based DRAM Testing Infrastructure
  https://github.com/CMU-SAFARI/SoftMC
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 457: Some Open Source Tools (II)
MQSim – A Fast Modern SSD Simulator
  https://github.com/CMU-SAFARI/MQSim
Mosaic – GPU Simulator Supporting Concurrent Applications
  https://github.com/CMU-SAFARI/Mosaic
IMPICA – Processing in 3D-Stacked Memory Simulator
  https://github.com/CMU-SAFARI/IMPICA
SMLA – Detailed 3D-Stacked Memory Simulator
  https://github.com/CMU-SAFARI/SMLA
HWASim – Simulator for Heterogeneous CPU-HWA Systems
  https://github.com/CMU-SAFARI/HWASim
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 458: More Open Source Tools (III)
A lot more open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 460: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 461: An Interview on Research and Education
Computing Research and Education (@ ISCA 2019)
  https://www.youtube.com/watch?v=8ffSEKZhmvo&list=PL5Q2soXY2Zi_4oP9LdL3cc8G6NIjD2Ydz
Maurice Wilkes Award Speech (10 minutes)
  https://www.youtube.com/watch?v=tcQ3zZ3JpuA&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=15

## Slide 462: More Thoughts and Suggestions
Onur Mutlu, "Some Reflections (on DRAM)" Award Speech for ACM SIGARCH Maurice Wilkes Award, at the ISCA Awards Ceremony, Phoenix, AZ, USA, 25 June 2019. [Slides (pptx) (pdf)] [Video of Award Acceptance Speech (Youtube; 10 minutes) (Youku; 13 minutes)] [Video of Interview after Award Acceptance (Youtube; 1 hour 6 minutes) (Youku; 1 hour 6 minutes)] [News Article on "ACM SIGARCH Maurice Wilkes Award goes to Prof. Onur Mutlu"]
Onur Mutlu, "How to Build an Impactful Research Group" 57th Design Automation Conference Early Career Workshop (DAC), Virtual, 19 July 2020. [Slides (pptx) (pdf)]

## Slide 463: End of Backup Slides