## Slide 1: Processing Data Where It Makes Sense in Modern Computing Systems: Enabling In-Memory Computation
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
17 September 2018
Cordoba HiPerNav Workshop 2018 Keynote

## Slide 2: Brief Self Introduction
Onur Mutlu
  Full Professor @ ETH Zurich CS, since September 2015
  Strecker Professor @ Carnegie Mellon University ECE/CS, 2009-2016, 2016-…
  PhD from UT-Austin, worked at Google, VMware, Microsoft Research, Intel, AMD
  https://people.inf.ethz.ch/omutlu/
  omutlu@gmail.com (Best way to reach me)
  https://people.inf.ethz.ch/omutlu/projects.htm
Research and Teaching in:
  Computer architecture, computer systems, hardware security, bioinformatics
  Memory and storage systems
  Hardware security, safety, predictability
  Fault tolerance
  Hardware/software cooperation
  Architectures for bioinformatics, health, medicine
  …

## Slide 3: Current Research Focus Areas
Research Focus: Computer architecture, HW/SW, bioinformatics, security
Memory and storage (DRAM, flash, emerging), interconnects
Heterogeneous & parallel systems, GPUs, systems for data analytics
System/architecture interaction, new execution models, new interfaces
Hardware security, energy efficiency, fault tolerance, performance
Genome sequence analysis & assembly algorithms and architectures
Biologically inspired systems & system design for bio/medicine
Graphics and Vision Processing
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
Broad research
spanning apps, systems, logic
with architecture at the center
Notes: Professor Mutlu’s research focus is all aspects of computer architecture, HW/SW interaction and bioinformatics.
He is looking for students to perform research in these areas.
He and his group, SAFARI, solve fundamental problems spanning:
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
His group does broad research spanning systems to logic with architecture at center

## Slide 4: Four Key Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency Architectures
Architectures for Genomics, Medicine, Health

## Slide 5: A Motivating Detour: Genome Sequence Analysis

## Slide 6: Our Dream
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
  Which of these DNAs does this DNA segment match with?
  What is the likely genetic disposition of this patient to this drug?
  . . .

## Slide 7: What Is a Genome Made Of?
Cell
Nucleus
The discovery of DNA’s double-helical structure (Watson+, 1953)
Notes: Unlocking the life’s code requires diving into the nucleus of our body cells, where the double-stranded genome resides. Genome is literally the 'code of life' - it is the set of instructions for making everything from you to zebras, strawberries, and even yeast.
since the discovery of dna’s double-helical structure (watson et al. 1953)

## Slide 8: DNA Under Electron Microscope
human chromosome #12
from HeLa’s cell
Notes: Henrietta Lacks,

## Slide 9: DNA Sequencing
Goal:
  Find the complete sequence of A, C, G, T’s in DNA.
Challenge:
  There is no machine that takes long DNA as an input, and gives the complete sequence as output
  All sequencing machines chop DNA into pieces and identify relatively small pieces (but not how they fit together)

## Slide 10: Untangling Yarn Balls & DNA Sequencing
Notes: untangling yarn ball

## Slide 11
Genome Sequencers
… and more! All produce data with different properties.
Roche/454
Illumina HiSeq2000
Ion Torrent PGM
Ion Torrent Proton
AB SOLiD
Oxford Nanopore GridION
Oxford Nanopore MinION
Complete
Genomics
Illumina MiSeq
Pacific Biosciences RS
Illumina
NovaSeq
6000

## Slide 12
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 13: Genome Sequence Alignment: Example
Source: By Aaron E. Darling, István Miklós, Mark A. Ragan - Figure 1 from Darling AE, Miklós I, Ragan MA (2008).
"Dynamics of Genome Rearrangement in Bacterial Populations". PLOS Genetics. DOI:10.1371/journal.pgen.1000128., CC BY 2.5, https://commons.wikimedia.org/w/index.php?curid=30550950

## Slide 14
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
300 M
bases/min
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Illumina HiSeq4000
2 M
bases/min
on average
(0.6%)
Bottlenecked in Mapping!!
Notes: Typical sequencer machine generates a flood of reads, for example, Illumina HiSeq4000 generates 300 million bases/minute.
However, existing computer alignment algorithms can only process 0.6% of these reads in the same amount of time.
This gap is widening as more advanced sequencers are made available in the market.

## Slide 15: Hash Table Based Read Mappers
+ Guaranteed to find all mappings  sensitive
+ Can tolerate up to e errors
http://mrfast.sourceforge.net/
Alkan+, "Personalized copy number and segmental duplication
maps using next-generation sequencing”, Nature Genetics 2009.
Notes: It turned out the Hash Table based mappers solve the first 2 challenges pretty well. They guarantee to find all mappings with no more than e errors present.

## Slide 16: Read Mapping Execution Time Breakdown
Chart: 
| candidate alignment locations (CAL) | SIMD banded Levenshtein edit distance | SAM printing
Time (sec) | 3738.88 | 81368.0945 | 2269.8755
Notes: An overwhelming majority of the read mapper’s execution time is spent in read alignment.

## Slide 17: Idea
Filter fast before you align
Minimize costly
“approximate string comparisons”

## Slide 18: Our First Filter: Pure Software Approach
Download source code and try for yourself
  Download link to FastHASH

## Slide 19: Shifted Hamming Distance: SIMD Acceleration
Xin+, "Shifted Hamming Distance: A Fast and Accurate SIMD-friendly Filter
to Accelerate Alignment Verification in Read Mapping”, Bioinformatics 2015.

## Slide 20
An Example Solution: GateKeeper
Alignment Filter
st
1
FPGA-based Alignment Filter.
Notes: To bridge the widening gap between the sequencer & the mapper, we propose the concept of pre-alignment filtering. We added a new examination step before the accurate alignment step. The main objective of this step is to detect the incorrect mappings accurately and rapidly. Only the mappings that pass our filter are examined by the alignment step. We also explore exploiting todays’ hardware accelerators to further boost the filtering speed of such filters.

## Slide 21: FPGA-Based Alignment Filtering
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 22: DNA Read Mapping & Filtering
Problem: Heavily bottlenecked by Data Movement
GateKeeper FPGA performance limited by DRAM bandwidth [Alser+, Bioinformatics 2017]
Ditto for SHD on SIMD [Xin+, Bioinformatics 2015]
Solution: Processing-in-memory can alleviate the bottleneck
However, we need to design mapping & filtering algorithms to fit processing-in-memory

## Slide 23: In-Memory DNA Sequence Analysis
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" BMC Genomics, 2018. Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. arxiv.org Version (pdf)

## Slide 24: Quick Note: Key Principles and Results
Alser et al., “GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA
Short Read Mapping,” Bioinformatics 2017.
Kim et al., “Genome Read In-Memory (GRIM) Filter,” BMC Genomics 2018.
Two key principles:
  Exploit the structure of the genome to minimize computation
  Morph and exploit the structure of the underlying hardware to maximize performance and efficiency
Algorithm-architecture co-design for DNA read mapping
  Speeds up read mapping by ~200X (sometimes more)
  Improves accuracy of read mapping in the presence of errors
Xin et al., “Accelerating Read Mapping with FastHASH,” BMC Genomics 2013.
Xin et al., “Shifted Hamming Distance: A Fast and Accurate SIMD-friendly Filter to Accelerate
Alignment Verification in Read Mapping,” Bioinformatics 2015.

## Slide 25: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION

## Slide 26: Nanopore Genome Assembly Pipeline
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly,” Briefings in Bioinformatics, 2018.

## Slide 27: More on Genome Analysis: Another Talk

## Slide 28: Recall Our Dream
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
Still a long ways to go
  Energy efficiency
  Performance (latency)
  Security
  Huge memory bottleneck

## Slide 29: Four Key Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency Architectures
Architectures for Genomics, Medicine, Health

## Slide 30: Memory & Storage

## Slide 31: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processors
and caches
Main Memory
Storage (SSD/HDD)

## Slide 32: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
FPGAs

## Slide 33: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
GPUs

## Slide 34: Memory System: A Shared Resource View
Storage
Most of the system is dedicated to storing and moving data

## Slide 35: State of the Main Memory System
Recent technology, architecture, and application trends
  lead to new requirements
  exacerbate old requirements
DRAM and memory controllers, as we know them today, are (will be) unlikely to satisfy all requirements
Some emerging non-volatile memory technologies (e.g., PCM) enable new opportunities: memory+storage merging
We need to rethink the main memory system
  to fix DRAM issues and enable emerging technologies
  to satisfy all requirements

## Slide 36: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 37: Major Trends Affecting Main Memory (II)
Need for main memory capacity, bandwidth, QoS increasing
  Multi-core: increasing number of cores/agents
  Data-intensive applications: increasing demand/hunger for data
  Consolidation: cloud computing, GPUs, mobile, heterogeneity
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 38: Example: The Memory Capacity Gap
Memory capacity per core expected to drop by 30% every two years
Trends worse for memory bandwidth per core!
Core count doubling ~ every 2 years
DRAM DIMM capacity doubling ~ every 3 years
Lim et al., ISCA 2009

## Slide 39: Example: Capacity, Bandwidth & Latency
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 40: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 41: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 42: Major Trends Affecting Main Memory (III)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
  ~40-50% energy spent in off-chip memory hierarchy [Lefurgy, IEEE Computer’03] >40% power in DRAM [Ware, HPCA’10][Paul,ISCA’15]
  DRAM consumes power even when not used (periodic refresh)
DRAM technology scaling is ending

## Slide 43: Major Trends Affecting Main Memory (IV)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending
  ITRS projects DRAM will not scale easily below X nm
  Scaling has provided many benefits:
    higher capacity (density), lower cost, lower energy

## Slide 44: Major Trends Affecting Main Memory (V)
DRAM scaling has already become increasingly difficult
  Increasing cell leakage current, reduced cell reliability, increasing manufacturing difficulties [Kim+ ISCA 2014], [Liu+ ISCA 2013], [Mutlu IMW 2013], [Mutlu DATE 2017]
  Difficult to significantly improve capacity, energy
Emerging memory technologies are promising
3D-Stacked DRAM | higher bandwidth | smaller capacity
Reduced-Latency DRAM (e.g., RLDRAM, TL-DRAM) | lower latency | higher cost
Low-Power DRAM (e.g., LPDDR3, LPDDR4) | lower power | higher latency higher cost
Non-Volatile Memory (NVM) (e.g., PCM, STTRAM, ReRAM, 3D Xpoint) | larger capacity | higher latency higher dynamic power lower endurance

## Slide 45: Major Trends Affecting Main Memory (V)
DRAM scaling has already become increasingly difficult
  Increasing cell leakage current, reduced cell reliability, increasing manufacturing difficulties [Kim+ ISCA 2014], [Liu+ ISCA 2013], [Mutlu IMW 2013], [Mutlu DATE 2017]
  Difficult to significantly improve capacity, energy
Emerging memory technologies are promising
3D-Stacked DRAM | higher bandwidth | smaller capacity
Reduced-Latency DRAM (e.g., RL/TL-DRAM, FLY-RAM) | lower latency | higher cost
Low-Power DRAM (e.g., LPDDR3, LPDDR4, Voltron) | lower power | higher latency higher cost
Non-Volatile Memory (NVM) (e.g., PCM, STTRAM, ReRAM, 3D Xpoint) | larger capacity | higher latency higher dynamic power lower endurance

## Slide 46: Major Trend: Hybrid Main Memory
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 47: Foreshadowing
Main Memory Needs
Intelligent Controllers

## Slide 48: Industry Is Writing Papers About It, Too

## Slide 49: Call for Intelligent Memory Controllers

## Slide 50: Agenda
Major Trends Affecting Main Memory
The Need for Intelligent Memory Controllers
  Bottom Up: Push from Circuits and Devices
  Top Down: Pull from Systems and Applications
Processing in Memory: Two Directions
  Minimally Changing Memory Chips
  Exploiting 3D-Stacked Memory
How to Enable Adoption of Processing in Memory
Conclusion

## Slide 51: Maslow’s (Human) Hierarchy of Needs
We need to start with reliability and security…
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.
Source: By User:Factoryjoe - Mazlow's Hierarchy of Needs.svg, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=7964065

## Slide 52: How Reliable/Secure/Safe is This Bridge?
Source: http://www.technologystudent.com/struct1/tacom1.png

## Slide 53: Collapse of the “Galloping Gertie”
Source: AP

## Slide 54: How Secure Are These People?
Source: https://s-media-cache-ak0.pinimg.com/originals/48/09/54/4809543a9c7700246a0cf8acdae27abf.jpg
Security is about preventing unforeseen consequences

## Slide 55: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 56: As Memory Scales, It Becomes Unreliable
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 57: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 58: Infrastructures to Understand Such Issues
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 59: Infrastructures to Understand Such Issues
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 60: SoftMC: Open Source DRAM Infrastructure
Hasan Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 61: SoftMC
https://github.com/CMU-SAFARI/SoftMC

## Slide 62: Data Retention in Memory [Liu et al., ISCA 2013]
Retention Time Profile of DRAM looks like this:
Location dependent
Stored value pattern dependent
Time dependent

## Slide 63: A Curious Discovery [Kim et al., ISCA 2014]
One can
predictably induce errors
in most DRAM memory chips

## Slide 64: DRAM RowHammer
A simple hardware failure mechanism
can create a widespread
system security vulnerability

## Slide 65: Modern DRAM is Prone to Disturbance Errors
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Hammered Row
Repeatedly reading a row enough times (before memory gets refreshed) induces disturbance errors in adjacent rows in most real DRAM chips you can buy today
Opened
Closed
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 66: Most DRAM Modules Are Vulnerable
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 67: Recent DRAM Is More Vulnerable
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 68: Recent DRAM Is More Vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 69: Recent DRAM Is More Vulnerable
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 70: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 71: A Simple Program Can Induce Many Errors
CPU
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Avoid cache hits
  Flush X from cache
Avoid row hits to X
  Read Y in another row
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 72: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 73: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 74: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 75: Observed Errors in Real Systems
A real reliability & security issue
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: When we executed the code on four different processors, all four of them yielded errors. Intel Haswell has the most errors, at 23 thousand, because it has the highest rate of accessing DRAM.
Later on, I’ll show that we can induce as many as ten million disturbance errors in a more controlled environment.
From this, we conclude that disturbance errors are a serious reliability issue.

## Slide 76: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)

## Slide 77: RowHammer Security Attack Example
“Rowhammer” is a problem with some recent DRAM devices in which repeatedly accessing a row of memory can cause bit flips in adjacent rows (Kim et al., ISCA 2014).
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
We tested a selection of laptops and found that a subset of them exhibited the problem.
We built two working privilege escalation exploits that use this effect.
  Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn+, 2015)
One exploit uses rowhammer-induced bit flips to gain kernel privileges on x86-64 Linux when run as an unprivileged userland process.
When run on a machine vulnerable to the rowhammer problem, the process was able to induce bit flips in page table entries (PTEs).
It was able to use this to gain write access to its own page table, and hence gain read-write access to all of physical memory.
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn & Dullien, 2015)

## Slide 78: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 79: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 80: More Security Implications (I)
Source: https://lab.dsst.io/32c3-slides/7197.html
Rowhammer.js: A Remote Software-Induced Fault Attack in JavaScript (DIMVA’16)
“We can gain unrestricted access to systems of website visitors.”

## Slide 81: More Security Implications (II)
Source: https://fossbytes.com/drammer-rowhammer-attack-android-root-devices/
Drammer: Deterministic Rowhammer Attacks on Mobile Platforms, CCS’16
  “Can gain control of a smart phone deterministically”

## Slide 82: More Security Implications (III)
Using an integrated GPU in a mobile system to remotely escalate privilege via the WebGL interface

## Slide 83: More Security Implications (IV)
Rowhammer over RDMA (I)

## Slide 84: More Security Implications (V)
Rowhammer over RDMA (II)

## Slide 85: More Security Implications?

## Slide 86: Apple’s Patch for RowHammer
https://support.apple.com/en-gb/HT204934
HP, Lenovo, and other vendors released similar patches

## Slide 87: Our Solution to RowHammer
PARA: Probabilistic Adjacent Row Activation
Key Idea
  After closing a row, we activate (i.e., refresh) one of its neighbors with a low probability: p = 0.005
Reliability Guarantee
  When p=0.005, errors in one year: 9.4×10-14
  By adjusting the value of p, we can vary the strength of protection against errors
Notes: We provide a more efficient solution, called PARA, which stands for probabilistic adjacent row activation.
The key idea is thus: after closing a row, we activate (i.e., refresh) one of its neighbors with a low probability, for example, p equal to 0.005.
PARA provides a strong reliability guarantee even under the worst-case access patterns to DRAM. When we set p to 0.005, the expected number of errors in one year is 9.4 times 10 to the negative 14. This probability is much lower the failure rate of other hardware components, for example, the hard-disk drive.
And by adjusting the value of p, PARA can provide an arbitrarily strong-degree of protection against errors.

## Slide 88: Advantages of PARA
PARA refreshes rows infrequently
  Low power
  Low performance-overhead
    Average slowdown: 0.20% (for 29 benchmarks)
    Maximum slowdown: 0.75%
PARA is stateless
  Low cost
  Low complexity
PARA is an effective and low-overhead solution to prevent disturbance errors
Notes: PARA has many advantages. Since it refreshes row infrequently, it has low power and low performance-overhead. Simulated across 29 benchmarks, we saw an average of only 0.2% slowdown and a maximum of only 0.75% slowdown.
In addition, due to its stateless nature, PARA has low cost and complexity.
Therefore, PARA is an effective and low-overhead solution to prevent disturbance errors.

## Slide 89: Probabilistic Activation in Real Life (I)
https://twitter.com/isislovecruft/status/1021939922754723841

## Slide 90: Probabilistic Activation in Real Life (II)
https://twitter.com/isislovecruft/status/1021939922754723841

## Slide 91: More on RowHammer Analysis
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data]

## Slide 92: Future of Memory Reliability
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 93: Industry Is Writing Papers About It, Too

## Slide 94: Call for Intelligent Memory Controllers

## Slide 95: Aside: Intelligent Controller for NAND Flash
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017,
PIEEE 2017, HPCA 2018, SIGMETRICS 2018]

## Slide 96: Aside: Intelligent Controller for NAND Flash
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 97: Takeaway
Main Memory Needs
Intelligent Controllers

## Slide 98: Agenda
Major Trends Affecting Main Memory
The Need for Intelligent Memory Controllers
  Bottom Up: Push from Circuits and Devices
  Top Down: Pull from Systems and Applications
Processing in Memory: Two Directions
  Minimally Changing Memory Chips
  Exploiting 3D-Stacked Memory
How to Enable Adoption of Processing in Memory
Conclusion

## Slide 99: Three Key Systems Trends
1. Data access is a major bottleneck
  Applications are increasingly data hungry
2. Energy consumption is a key limiter
3. Data movement energy dominates compute
  Especially true for off-chip to on-chip movement

## Slide 100: The Need for More Memory Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 101: Do We Want This?
Source: V. Milutinovic

## Slide 102: Or This?
Source: V. Milutinovic

## Slide 103: Maslow’s (Human) Hierarchy of Needs, Revisited
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Everlasting energy
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.

## Slide 104: Challenge and Opportunity for Future
High Performance,
Energy Efficient,
Sustainable

## Slide 105: The Problem
Data access is the major performance and energy bottleneck
Our current
design principles
cause great energy waste
(and great performance loss)

## Slide 106: The Problem
Processing of data
is performed
far away from the data

## Slide 107: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 108: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 109: Today’s Computing Systems
Are overwhelmingly processor centric
All data processed in the processor  at great system cost
Processor is heavily optimized and is considered the master
Data storage units are dumb and are largely unoptimized (except for some that are on the processor die)

## Slide 110: Yet …
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 111: The Performance Perspective
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors" Proceedings of the 9th International Symposium on High-Performance Computer Architecture (HPCA), pages 129-140, Anaheim, CA, February 2003. Slides (pdf)

## Slide 112: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 113: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 114: Perils of Processor-Centric Design
Grossly-imbalanced systems
  Processing done only in one place
  Everything else just stores and moves data: data moves a lot
   Energy inefficient
   Low performance
   Complex
Overly complex and bloated processor (and accelerators)
  To tolerate data access from memory
  Complex hierarchies and mechanisms
   Energy inefficient
   Low performance
   Complex

## Slide 115: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data

## Slide 116: The Energy Perspective
Dally, HiPEAC 2015

## Slide 117: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 118: Data Movement vs. Computation Energy
Data movement is a major system energy bottleneck
  Comprises 41% of mobile system energy during web browsing [2]
  Costs ~115 times as much energy as an ADD operation [1, 2]
[1]: Reducing data Movement Energy via Online Data Clustering and Encoding (MICRO’16)
[2]: Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms (IISWC’14)

## Slide 119: Energy Waste in Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 120: We Do Not Want to Move Data!
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 121: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 122: Goal: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processor chip and in-memory units?
  software and hardware interfaces?
  system software and languages?
  algorithms?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 123: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
Pull from Systems and Applications
  Data access is a major system and application bottleneck
  Systems are energy limited
  Data movement much more energy-hungry than computation
Dally, HiPEAC 2015

## Slide 124: Agenda
Major Trends Affecting Main Memory
The Need for Intelligent Memory Controllers
  Bottom Up: Push from Circuits and Devices
  Top Down: Pull from Systems and Applications
Processing in Memory: Two Directions
  Minimally Changing Memory Chips
  Exploiting 3D-Stacked Memory
How to Enable Adoption of Processing in Memory
Conclusion

## Slide 125: Processing in Memory: Two Approaches
1. Minimally changing memory chips
2. Exploiting 3D-stacked memory

## Slide 126: Approach 1: Minimally Changing DRAM
DRAM has great capability to perform bulk data movement and computation internally with small changes
  Can exploit internal connectivity to move data
  Can exploit analog computation capability
  …
Examples: RowClone, In-DRAM AND/OR, Gather/Scatter DRAM
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)
  "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology” (Seshadri et al., MICRO 2017)

## Slide 127: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 128: Today’s Systems: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 129: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 130: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 131: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 132: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 133: Memory as an Accelerator
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 134: In-Memory Bulk Bitwise Operations
We can support in-DRAM COPY, ZERO, AND, OR, NOT, MAJ
At low cost
Using analog computation capability of DRAM
  Idea: activating multiple rows performs computation
30-60X performance and energy improvement
  Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
New memory technologies enable even more opportunities
  Memristors, resistive RAM, phase change mem, STT-MRAM, …
  Can operate on data with minimal movement

## Slide 135: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 136: In-DRAM NOT: Dual Contact Cell
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
Idea:
Feed the
negated value
in the sense amplifier
into a special row

## Slide 137: Performance: In-DRAM Bitwise Operations
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 138: Energy of In-DRAM Bitwise Operations
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 139: Ambit vs. DDR3: Performance and Energy
Chart: 
| not | and/or | nand/nor | xor/xnor | mean
Performance Improvement | 51.6251 | 38.3193 | 30.6965 | 21.8566 | 32
Energy Reduction | 59.5 | 43.9 | 35.1 | 25.1 | 35
32X
35X
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 140: Bulk Bitwise Operations in Workloads
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017

## Slide 141: Example Data Structure: Bitmap Index
Alternative to B-tree and its variants
Efficient for performing range queries and joins
Many bitwise operations to perform a query
Bitmap 1
Bitmap 2
Bitmap 4
Bitmap 3
age < 18
18 < age < 25
25 < age < 60
age > 60

## Slide 142: Performance: Bitmap Index on Ambit
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 143: Performance: BitWeaving on Ambit
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 144: More on In-DRAM Bulk AND/OR
Vivek Seshadri, Kevin Hsieh, Amirali Boroumand, Donghyuk Lee, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Fast Bulk Bitwise AND and OR in DRAM" IEEE Computer Architecture Letters (CAL), April 2015.

## Slide 145: More on Ambit
Vivek Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.

## Slide 146: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 147: Challenge: Intelligent Memory Device
Does memory
have to be
dumb?

## Slide 148: Agenda
Major Trends Affecting Main Memory
The Need for Intelligent Memory Controllers
  Bottom Up: Push from Circuits and Devices
  Top Down: Pull from Systems and Applications
Processing in Memory: Two Directions
  Minimally Changing Memory Chips
  Exploiting 3D-Stacked Memory
How to Enable Adoption of Processing in Memory
Conclusion

## Slide 149: Processing in Memory: Two Approaches
1. Minimally changing memory chips
2. Exploiting 3D-stacked memory

## Slide 150: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 151: DRAM Landscape (circa 2015)
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.

## Slide 152: Two Key Questions in 3D-Stacked PIM
How can we accelerate important applications if we use 3D-stacked memory as a coarse-grained accelerator?
  what is the architecture and programming model?
  what are the mechanisms for acceleration?
What is the minimal processing-in-memory support we can provide?
  without changing the system significantly
  while achieving significant benefits

## Slide 153: Graph Processing
Large graphs are everywhere (circa 2015)
Scalable large-scale graph processing is challenging
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos
Chart: Speedup
| 128 Cores | 32 Cores
열3 | 1.4206 | 1

## Slide 154: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 155: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 156: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communications via Remote Function Calls

## Slide 157: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 158: Communications In Tesseract (I)

## Slide 159: Communications In Tesseract (II)

## Slide 160: Communications In Tesseract (III)

## Slide 161: Remote Function Call (Non-Blocking)

## Slide 162: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
Tesseract
32 Tesseract Cores
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 163: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
On five graph processing algorithms

## Slide 164: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
Chart: Memory Bandwidth Consumption
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 0.079545 | 0.1904 | 0.24289 | 1.2943 | 2.244 | 2.9197

## Slide 165: Tesseract Graph Processing System Energy
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
> 8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 166: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 167: PIM on Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.

## Slide 168: Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Amirali Boroumand
Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun,
Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu

## Slide 169: Consumer Devices
Consumer devices are everywhere!
Energy consumption is a first-class concern in consumer devices
Notes: Consumer devices like tablets smartphone and wearable are now everywhere and used by billions of people.
One of the major challenge in these devices is battery limitation which makes the energy consumption a critical concern …

## Slide 170: Popular Google Consumer Workloads
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 171: Energy Cost of Data Movement
Data Movement
1st key observation: 62.7% of the total system energy is spent on data movement
  Potential solution: move computation close to data
  Challenge: limited area and energy budget
Processing-In-Memory (PIM)
SoC
DRAM
L2
L1
CPU
CPU
CPU
CPU
Compute Unit
Notes: Throughout our analysis, we make a key observation that out of all sources of energy consumption, data movement is a major contributor to the total system energy. We find that across all of the workloads, on average around 62.7% of total system energy is spent on data movement.
One way to reduce data movement cost is to move computation close to data, or …
One potential solution to address this cost it do move computation close to data, or in other words, do procesing in memory. However, the challenge is that these devices.
One potential solution to mitigate data movement cost and reduce total system energy is to execute data-movement heavy portions of application close to data, or in other words, do processing in memory. However, consumer devices are extermely limited in terms of area and power budget. So the question is can we move part of the data movement heavy portion given the limited area and energy budget. Our

## Slide 172: Using PIM to Reduce Data Movement
  2nd key observation: a significant fraction of the data movement often comes from simple functions
PIM Core
PIM Accelerator
PIM Accelerator
PIM Accelerator
We can design lightweight logic to implement these simple functions in memory
Small embedded low-power core
Small fixed-function accelerators
  Offloading to PIM logic reduces energy and improves performance, on average, by 55.4% and 54.2%
Notes: To figure out if we can use processing in memory, we dig deeper into our analysis and we make another key observation that majority of data movement often comes form simple functions and pritmitives. We find that these simple function can be implemented in memory as either a small embedded core, or group of small fixed function accelerators. Our result shows that offloading these function to PIM logic can significantly reduce data movement for each function and reduce energy on average around 55% and improve perforamcne around 54%.
our PIM core can reduce significant portion of data movement, reduce enregy by 49.1% for each function and improve performance up to 2.2X. While using group of fixed function accelerator reduce energy by 55.4% and improve performance by up to 2.5X.
  Or use Saugata’s approach : Reduces total system energy by an average of 55.4%
  Reduces execution time by an average of 54.2%
Our result show that both of them can significantly reduce the data movement for each function.
Feedback: talk about result more
Don’t talk about specific detail like MemCopy, MemSet stuff like that
Main take away: data movement come from simple functions that are simple enough to implement in PIM
We find that these functions and primitves can be implemented as PIM logic using either (1) a small low-power general-purpose embedded core or (2) a group of small fixed-function accelerators (PIM accelerators). Our Analysis shows that both are cost-feasible to use in consumer devices. We find that they eliminate a significant fraction of dat amovement, and reduce energy consumption for each of these operation on average by 49 and 55%.

## Slide 173: Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Amirali Boroumand
Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun,
Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu
ASPLOS 2018
Notes: Please drop by our talk during session 1 if you would like to learn more about data movement in Google workloads.

## Slide 174: More on PIM for Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 175: Truly Distributed GPU Processing with PIM?
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
SM (Streaming Multiprocessor)

## Slide 176: Accelerating GPU Execution with PIM (I)
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 177: Accelerating GPU Execution with PIM (II)
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 178: Accelerating Linked Data Structures
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 179: Accelerating Dependent Cache Misses
Milad Hashemi, Khubaib, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "Accelerating Dependent Cache Misses with an Enhanced Memory Controller" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 180: Two Key Questions in 3D-Stacked PIM
How can we accelerate important applications if we use 3D-stacked memory as a coarse-grained accelerator?
  what is the architecture and programming model?
  what are the mechanisms for acceleration?
What is the minimal processing-in-memory support we can provide?
  without changing the system significantly
  while achieving significant benefits

## Slide 181: PEI: PIM-Enabled Instructions (Ideas)
Goal: Develop mechanisms to get the most out of near-data processing with minimal cost, minimal changes to the system, no changes to the programming model
Key Idea 1: Expose each PIM operation as a cache-coherent, virtually-addressed host processor instruction (called PEI) that operates on only a single cache block
  e.g., __pim_add(&w.next_rank, value)  pim.add r1, (r2)
  No changes sequential execution/programming model
  No changes to virtual memory
  Minimal changes to cache coherence
  No need for data mapping: Each PEI restricted to a single memory module
Key Idea 2: Dynamically decide where to execute a PEI (i.e., the host processor or PIM accelerator) based on simple locality characteristics and simple hardware predictors
  Execute each operation at the location that provides the best performance

## Slide 182: Simple PIM Operations as ISA Extensions (II)
Main Memory
w.next_rank
w.next_rank
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}
Host Processor
w.next_rank
w.next_rank
64 bytes in
64 bytes out
Conventional Architecture

## Slide 183: Simple PIM Operations as ISA Extensions (III)
Main Memory
w.next_rank
w.next_rank
Host Processor
value
8 bytes in
0 bytes out
In-Memory Addition
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pim.add r1, (r2)

## Slide 184: PEI: PIM-Enabled Instructions (Example)
Executed either in memory or in the processor: dynamic decision
  Low-cost locality monitoring for a single instruction
Cache-coherent, virtually-addressed, single cache block only
Atomic between different PEIs
Not atomic with normal instructions (use pfence for ordering)
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pfence();
pim.add r1, (r2)
pfence

## Slide 185: Example (Abstract) PEI uArchitecture
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
3D-stacked Memory
…
PCU (PEI Computation Unit)
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU (PEI
Mgmt Unit)
Example PEI uArchitecture

## Slide 186: PEI: Initial Evaluation Results
Initial evaluations with 10 emerging data-intensive workloads
  Large-scale graph processing
  In-memory data analytics
  Machine learning and data mining
  Three input sets (small, medium, large) for each workload to analyze the impact of data locality
Pin-based cycle-level x86-64 simulation
  Performance Improvement and Energy Reduction:
    47% average speedup with large input data sets
    32% speedup with small input data sets
    25% avg. energy reduction in a single node with large input data sets

## Slide 187: Simpler PIM: PIM-Enabled Instructions
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 188: Automatic Code and Data Mapping
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 189: Automatic Offloading of Critical Code
Milad Hashemi, Khubaib, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "Accelerating Dependent Cache Misses with an Enhanced Memory Controller" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 190: Automatic Offloading of Prefetch Mechanisms
Milad Hashemi, Onur Mutlu, and Yale N. Patt, "Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads" Proceedings of the 49th International Symposium on Microarchitecture (MICRO), Taipei, Taiwan, October 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pdf)] [Poster (pptx) (pdf)]

## Slide 191: Efficient Automatic Data Coherence Support
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 192: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 193: Challenge and Opportunity for Future
Fundamentally
High-Performance
(Data-Centric)
Computing Architectures

## Slide 194: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 195: Agenda
Major Trends Affecting Main Memory
The Need for Intelligent Memory Controllers
  Bottom Up: Push from Circuits and Devices
  Top Down: Pull from Systems and Applications
Processing in Memory: Two Directions
  Minimally Changing Memory Chips
  Exploiting 3D-Stacked Memory
How to Enable Adoption of Processing in Memory
Conclusion

## Slide 196: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 197: Barriers to Adoption of PIM
1. Functionality of and applications for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System support: coherence & virtual memory
4. Runtime systems for adaptive scheduling, data mapping, access/sharing control
5. Infrastructures to assess benefits and feasibility

## Slide 198: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 199: Open Problems: PIM Adoption
Saugata Ghose, Kevin Hsieh, Amirali Boroumand, Rachata Ausavarungnirun, Onur Mutlu, "Enabling the Adoption of Processing-in-Memory: Challenges, Mechanisms, Future Research Directions" Invited Book Chapter, to appear in 2018. [Preliminary arxiv.org version]
https://arxiv.org/pdf/1802.00320.pdf

## Slide 200: Key Challenge 1: Code Mapping
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
?
Main GPU
3D-stacked memory
(memory stack)
Challenge 1: Which operations should be executed in memory vs. in CPU?
?
SM (Streaming Multiprocessor)

## Slide 201: Key Challenge 2: Data Mapping
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
Challenge 2: How should data be mapped to different 3D memory stacks?
SM (Streaming Multiprocessor)

## Slide 202: How to Do the Code and Data Mapping?
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 203: How to Schedule Code?
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 204: Challenge: Coherence for Hybrid CPU-PIM Apps
Traditional
coherence
No coherence
overhead

## Slide 205: How to Maintain Coherence?
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 206: How to Support Virtual Memory?
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 207: How to Design Data Structures for PIM?
Zhiyu Liu, Irina Calciu, Maurice Herlihy, and Onur Mutlu, "Concurrent Data Structures for Near-Memory Computing" Proceedings of the 29th ACM Symposium on Parallelism in Algorithms and Architectures (SPAA), Washington, DC, USA, July 2017. [Slides (pptx) (pdf)]

## Slide 208: Simulation Infrastructures for PIM
Ramulator extended for PIM
  Flexible and extensible DRAM simulator
  Can model many different memory standards and proposals
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.
  https://github.com/CMU-SAFARI/ramulator

## Slide 209: An FPGA-based Test-bed for PIM?
Hasan Hassan et al., SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 210: Simulation Infrastructures for PIM (in SSDs)
Arash Tavakkol, Juan Gomez-Luna, Mohammad Sadrosadati, Saugata Ghose, and Onur Mutlu, "MQSim: A Framework for Enabling Realistic Studies of Modern Multi-Queue SSD Devices" Proceedings of the 16th USENIX Conference on File and Storage Technologies (FAST), Oakland, CA, USA, February 2018. [Slides (pptx) (pdf)] [Source Code]

## Slide 211: New Applications and Use Cases for PIM
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" BMC Genomics, 2018. Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. arxiv.org Version (pdf)

## Slide 212: Genome Read In-Memory (GRIM) Filter: Fast Seed Location Filtering in DNA Read Mapping using Processing-in-Memory Technologies
Jeremie Kim,
Damla Senol, Hongyi Xin, Donghyuk Lee,
Saugata Ghose, Mohammed Alser, Hasan Hassan,
Oguz Ergin, Can Alkan, and Onur Mutlu
Notes: Hello, my name is Jeremie Kim and I will be presenting Genome Read In-Memory Filter which will also be referred to as GRIM-Filter for short.
[CLICK]

## Slide 213: Executive Summary
Genome Read Mapping is a very important problem and is the first step in many types of genomic analysis
  Could lead to improved health care, medicine, quality of life
Read mapping is an approximate string matching problem
  Find the best fit of 100 character strings into a 3 billion character dictionary
  Alignment is currently the best method for determining the similarity between two strings, but is very expensive
We propose an in-memory processing algorithm GRIM-Filter for accelerating read mapping, by reducing the number of required alignments
We implement GRIM-Filter using in-memory processing within 3D-stacked memory and show up to 3.7x speedup.

## Slide 214: Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Amirali Boroumand
Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun,
Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu

## Slide 215: Open Problems: PIM Adoption
Saugata Ghose, Kevin Hsieh, Amirali Boroumand, Rachata Ausavarungnirun, Onur Mutlu, "Enabling the Adoption of Processing-in-Memory: Challenges, Mechanisms, Future Research Directions" Invited Book Chapter, to appear in 2018. [Preliminary arxiv.org version]
https://arxiv.org/pdf/1802.00320.pdf

## Slide 216: Enabling the Paradigm Shift

## Slide 217: Computer Architecture Today
You can revolutionize the way computers are built, if you understand both the hardware and the software (and change each accordingly)
You can invent new paradigms for computation, communication, and storage
Recommended book: Thomas Kuhn, “The Structure of Scientific Revolutions” (1962)
  Pre-paradigm science: no clear consensus in the field
  Normal science: dominant theory used to explain/improve things (business as usual); exceptions considered anomalies
  Revolutionary science: underlying assumptions re-examined

## Slide 218: Computer Architecture Today
You can revolutionize the way computers are built, if you understand both the hardware and the software (and change each accordingly)
You can invent new paradigms for computation, communication, and storage
Recommended book: Thomas Kuhn, “The Structure of Scientific Revolutions” (1962)
  Pre-paradigm science: no clear consensus in the field
  Normal science: dominant theory used to explain/improve things (business as usual); exceptions considered anomalies
  Revolutionary science: underlying assumptions re-examined

## Slide 219: Agenda
Major Trends Affecting Main Memory
The Need for Intelligent Memory Controllers
  Bottom Up: Push from Circuits and Devices
  Top Down: Pull from Systems and Applications
Processing in Memory: Two Directions
  Minimally Changing Memory Chips
  Exploiting 3D-Stacked Memory
How to Enable Adoption of Processing in Memory
Conclusion

## Slide 220: Four Key Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency Architectures
Architectures for Genomics, Medicine, Health

## Slide 221: Maslow’s Hierarchy of Needs, A Third Time
Speed
Speed
Speed
Speed
Speed
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.

## Slide 222: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 223: Challenge and Opportunity for Future
Fundamentally
Low-Latency
(Data-Centric)
Computing Architectures

## Slide 224: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 225: One Important Takeaway
Main Memory Needs
Intelligent Controllers

## Slide 226: Concluding Remarks

## Slide 227: A Quote from A Famous Architect
“architecture […] based upon principle, and not upon precedent”

## Slide 228: Precedent-Based Design?
“architecture […] based upon principle, and not upon precedent”

## Slide 229: Principled Design
“architecture […] based upon principle, and not upon precedent”

## Slide 231: The Overarching Principle

## Slide 232: Another Example: Precedent-Based Design
Source: http://cookiemagik.deviantart.com/art/Train-station-207266944

## Slide 233: Principled Design
Source: By Toni_V, CC BY-SA 2.0, https://commons.wikimedia.org/w/index.php?curid=4087256

## Slide 234: Another Principled Design
Source: By Martín Gómez Tagle - Lisbon, Portugal, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=13764903
Source: http://www.arcspace.com/exhibitions/unsorted/santiago-calatrava/

## Slide 235: Another Principled Design
Source: De Galván - Puente del Alamillo.jpg on Enciclopedia.us.es, GFDL, https://commons.wikimedia.org/w/index.php?curid=15026095

## Slide 236: Principle Applied to Another Structure
Source: https://www.dezeen.com/2016/08/29/santiago-calatrava-oculus-world-trade-center-transportation-hub-new-york-photographs-hufton-crow/
Source: By 準建築人手札網站 Forgemind ArchiMedia - Flickr: IMG_2489.JPG, CC BY 2.0,
https://commons.wikimedia.org/w/index.php?curid=31493356, https://en.wikipedia.org/wiki/Santiago_Calatrava

## Slide 237: The Overarching Principle

## Slide 238: Overarching Principle for Computing?
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 239: Concluding Remarks
It is time to design principled system architectures to solve the memory problem
Design complete systems to be balanced, high-performance, and energy-efficient, i.e., data-centric (or memory-centric)
Enable computation capability inside and close to memory
This can
  Lead to orders-of-magnitude improvements
  Enable new applications & computing platforms
  Enable better understanding of nature
  …
Notes: Perhaps we have taken processor-centric system design a bit too far

## Slide 240: The Future of Processing in Memory is Bright
Regardless of challenges
  in underlying technology and overlying problems/requirements
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Can enable:
- Orders of magnitude
improvements
- New applications and
computing systems
Yet, we have to
- Think across the stack
- Design enabling systems

## Slide 241: If In Doubt, See Other Doubtful Technologies
A very “doubtful” emerging technology
  for at least two decades
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 242: For Some Open Problems, See
Saugata Ghose, Kevin Hsieh, Amirali Boroumand, Rachata Ausavarungnirun, Onur Mutlu, "Enabling the Adoption of Processing-in-Memory: Challenges, Mechanisms, Future Research Directions" Invited Book Chapter, to appear in 2018. [Preliminary arxiv.org version]
https://arxiv.org/pdf/1802.00320.pdf

## Slide 243: Accelerated Memory Course (~6.5 hours)
ACACES 2018
  Memory Systems and Memory-Centric Computing Systems
  Taught by Onur Mutlu July 9-13, 2018
  ~6.5 hours of lectures
Website for the Course including Videos, Slides, Papers
  https://people.inf.ethz.ch/omutlu/acaces2018.html
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi-HXxomthrpDpMJm05P6J9x
All Papers are at:
  https://people.inf.ethz.ch/omutlu/projects.htm
  Final lecture notes and readings (for all topics)

## Slide 244: Processing Data Where It Makes Sense in Modern Computing Systems: Enabling In-Memory Computation
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
17 September 2018
Cordoba HiPerNav Workshop 2018 Keynote

## Slide 245: Slides Not Covered But Could Be Useful

## Slide 246: Readings, Videos, Reference Materials

## Slide 247: Accelerated Memory Course (~6.5 hours)
ACACES 2018
  Memory Systems and Memory-Centric Computing Systems
  Taught by Onur Mutlu July 9-13, 2018
  ~6.5 hours of lectures
Website for the Course including Videos, Slides, Papers
  https://people.inf.ethz.ch/omutlu/acaces2018.html
  https://www.youtube.com/playlist?list=PL5Q2soXY2Zi-HXxomthrpDpMJm05P6J9x
All Papers are at:
  https://people.inf.ethz.ch/omutlu/projects.htm
  Final lecture notes and readings (for all topics)

## Slide 248: Reference Overview Paper I
Saugata Ghose, Kevin Hsieh, Amirali Boroumand, Rachata Ausavarungnirun, Onur Mutlu, "Enabling the Adoption of Processing-in-Memory: Challenges, Mechanisms, Future Research Directions" Invited Book Chapter, to appear in 2018. [Preliminary arxiv.org version]
https://arxiv.org/pdf/1802.00320.pdf

## Slide 249: Reference Overview Paper II
Onur Mutlu and Lavanya Subramanian, "Research Problems and Opportunities in Memory Systems" Invited Article in Supercomputing Frontiers and Innovations (SUPERFRI), 2014/2015.
https://people.inf.ethz.ch/omutlu/pub/memory-systems-research_superfri14.pdf

## Slide 250: Reference Overview Paper III
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 251: Reference Overview Paper IV
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Technical talk at MemCon 2013 (MEMCON), Santa Clara, CA, August 2013. [Slides (pptx) (pdf)] [Video] [Coverage on StorageSearch]
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 252: Reference Overview Paper V
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 253: Related Videos and Course Materials (I)
Undergraduate Computer Architecture Course Lecture Videos (2015, 2014, 2013)
Undergraduate Computer Architecture Course Materials (2015, 2014, 2013)
Graduate Computer Architecture Course Lecture Videos (2017, 2015, 2013)
Graduate Computer Architecture Course Materials (2017, 2015, 2013)
Parallel Computer Architecture Course Materials (Lecture Videos)

## Slide 254: Related Videos and Course Materials (II)
Freshman Digital Circuits and Computer Architecture Course Lecture Videos (2018, 2017)
Freshman Digital Circuits and Computer Architecture Course Materials (2018)
Memory Systems Short Course Materials
(Lecture Video on Main Memory and DRAM Basics)

## Slide 255: Some Open Source Tools (I)
Rowhammer – Program to Induce RowHammer Errors
  https://github.com/CMU-SAFARI/rowhammer
Ramulator – Fast and Extensible DRAM Simulator
  https://github.com/CMU-SAFARI/ramulator
MemSim – Simple Memory Simulator
  https://github.com/CMU-SAFARI/memsim
NOCulator – Flexible Network-on-Chip Simulator
  https://github.com/CMU-SAFARI/NOCulator
SoftMC – FPGA-Based DRAM Testing Infrastructure
  https://github.com/CMU-SAFARI/SoftMC
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 256: Some Open Source Tools (II)
MQSim – A Fast Modern SSD Simulator
  https://github.com/CMU-SAFARI/MQSim
Mosaic – GPU Simulator Supporting Concurrent Applications
  https://github.com/CMU-SAFARI/Mosaic
IMPICA – Processing in 3D-Stacked Memory Simulator
  https://github.com/CMU-SAFARI/IMPICA
SMLA – Detailed 3D-Stacked Memory Simulator
  https://github.com/CMU-SAFARI/SMLA
HWASim – Simulator for Heterogeneous CPU-HWA Systems
  https://github.com/CMU-SAFARI/HWASim
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 257: More Open Source Tools (III)
A lot more open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 258: Referenced Papers
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en
  https://people.inf.ethz.ch/omutlu/acaces2018.html

## Slide 259: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 260: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 261: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 262: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 263: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 264: Tesseract: Extra Slides

## Slide 265: Communications In Tesseract (I)

## Slide 266: Communications In Tesseract (II)

## Slide 267: Communications In Tesseract (III)

## Slide 268: Remote Function Call (Non-Blocking)

## Slide 269: Effect of Bandwidth & Programming Model
Chart: Speedup
| HMC-MC | HMC-MC + PIM BW | Tesseract + Conventional BW | Tesseract
계열 1 | 1 | 2.3043 | 3.0224 | 6.4999
HMC-MC Bandwidth (640GB/s)
Tesseract Bandwidth (8TB/s)
Bandwidth
Programming Model
(No Prefetching)

## Slide 270: Reducing Memory Latency

## Slide 271: Main Memory Latency Lags Behind
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 272: A Closer Look …
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 273: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 274: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 275: Why the Long Latency?
Design of DRAM uArchitecture
  Goal: Maximize capacity/area, not minimize latency
“One size fits all” approach to latency specification
  Same latency parameters for all temperatures
  Same latency parameters for all DRAM chips (e.g., rows)
  Same latency parameters for all parts of a DRAM chip
  Same latency parameters for all supply voltage levels
  Same latency parameters for all application data
  …

## Slide 276: Latency Variation in Memory Chips
High
Low
DRAM Latency
DRAM B
DRAM A
DRAM C
Slow cells
Heterogeneous manufacturing & operating conditions → latency variation in timing parameters

## Slide 277: DRAM Characterization Infrastructure
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 278: DRAM Characterization Infrastructure
Hasan Hassan et al., SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies, HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 279: SoftMC: Open Source DRAM Infrastructure
https://github.com/CMU-SAFARI/SoftMC

## Slide 280: Tackling the Fixed Latency Mindset
Reliable operation latency is actually very heterogeneous
  Across temperatures, chips, parts of a chip, voltage levels, …
Idea: Dynamically find out and use the lowest latency one can reliably access a memory location with
  Adaptive-Latency DRAM [HPCA 2015]
  Flexible-Latency DRAM [SIGMETRICS 2016]
  Design-Induced Variation-Aware DRAM [SIGMETRICS 2017]
  Voltron [SIGMETRICS 2017]
  ...
We would like to find sources of latency heterogeneity and exploit them to minimize latency

## Slide 281: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer provides multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 282
Latency Reduction Summary of 115 DIMMs
Latency reduction for read & write (55°C)
  Read Latency: 32.7%
  Write Latency: 55.1%
Latency reduction for each timing parameter (55°C)
  Sensing: 17.3%
  Restore: 37.3% (read), 54.8% (write)
  Precharge: 35.2%
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 283
AL-DRAM: Real System Evaluation
System
  CPU: AMD 4386 ( 8 Cores, 3.1GHz, 8MB LLC)
  DRAM: 4GByte DDR3-1600 (800Mhz Clock)
  OS: Linux
  Storage: 128GByte SSD
Workload
  35 applications from SPEC, STREAM, Parsec, Memcached, Apache, GUPS

## Slide 284
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
1.4%
6.7%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
5.0%
AL-DRAM: Single-Core Evaluation
AL-DRAM improves single-core performance
on a real system
Performance Improvement
Average
Improvement
all-35-workload

## Slide 285
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
AL-DRAM: Multi-Core Evaluation
AL-DRAM provides higher performance on
multi-programmed & multi-threaded workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 286: Reducing Latency Also Reduces Energy
AL-DRAM reduces DRAM power consumption by 5.8%
Major reason: reduction in row activation time

## Slide 287: More on Adaptive-Latency DRAM
Donghyuk Lee, Yoongu Kim, Gennady Pekhimenko, Samira Khan, Vivek Seshadri, Kevin Chang, and Onur Mutlu, "Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)] [Full data sets]

## Slide 288: Heterogeneous Latency within A Chip
Chart: 40 Workloads
Baseline (DDR3) | 1
FLY-DRAM (D1) | 1.133
FLY-DRAM (D2) | 1.176
FLY-DRAM (D3) | 1.195
Upper Bound | 1.197
17.6%
19.5%
19.7%
13.3%
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 289: Analysis of Latency Variation in DRAM Chips
Kevin Chang, Abhijith Kashyap, Hasan Hassan, Samira Khan, Kevin Hsieh, Donghyuk Lee, Saugata Ghose, Gennady Pekhimenko, Tianshi Li, and Onur Mutlu, "Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Antibes Juan-Les-Pins, France, June 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 290
Inherently fast
inherently slow
What Is Design-Induced Variation?
slow
fast
slow
fast
Systematic variation in cell access times
caused by the physical organization of DRAM
sense amplifiers
wordline drivers
across row
distance from sense amplifier
across column
distance from wordline driver
Notes: As we described, cells in a mat have different distances from peripheral logic.
Cells in different rows have different distance from the sense amplifiers.
Cells in different columns have different distance from the wordline drivers.
Therefore, some regions are inherently faster than other regions,
and some regions are inherently slower than other regions.
We call this architectural variation.

## Slide 291
DIVA Online Profiling
inherently slow
Profile only slow regions to determine min. latency
 Dynamic & low cost latency optimization
sense amplifier
wordline driver
Design-Induced-Variation-Aware
Notes: We propoe AVA Online profiling.
The key idea is profiling only slow regions to determine latency, leading to low cost online DRAM test.

## Slide 292
inherently slow
DIVA Online Profiling
slow cells
design-induced
variation
process
variation
localized error
random error
online profiling
error-correcting code
Combine error-correcting codes & online profiling
 Reliably reduce DRAM latency
sense amplifier
wordline driver
Design-Induced-Variation-Aware
Notes: However, due to the process variation, some cells are more vulnerable than other cells, as the figure show.
These cells are randomly distributed while cells in the slow regions cause localized error.
To address both type of cells,
We integrate conventional ECC to correct the process variation induced errors.
Therefore, combining ECC and online profiling leads to reliably reducing DRAM latency.

## Slide 293
DIVA-DRAM Reduces Latency
Read
Write
Chart: 
| 55°C | 85°C | 55°C | 85°C | 55°C | 85°C | AL-DRAM | AVA Profiling | AVA Profiling + Shuffling
Latency Reduction | 0.31202 | 0.25527 | 0.35118 | 0.3464 | 0.36569 | 0.358
Latency Reduction
DIVA
DIVA
Chart: 
| 55°C | 85°C | 55°C | 85°C | 55°C | 85°C | AL-DRAM | AVA Profiling | AVA Profiling + Shuffling
Latency Reduction | 0.36561 | 0.27539 | 0.394 | 0.38718 | 0.41294 | 0.40274
DIVA
DIVA
DIVA-DRAM reduces latency more aggressively and uses ECC to correct random slow cells
Notes: The figure compares latency reduction by using AL-DRAM, AVA Profiling, and both AVA Profiling and Shuffling.
As we can, using AVA profiling and shuffling enables more latency reduction compared to AL-DRAM.
This is mainly because ECC corrects the worst cells in a DRAM module, reducing more latency.
Therefore, we conclude that AVA-DRAM reduces latency significantly.

## Slide 294: Design-Induced Latency Variation in DRAM
Donghyuk Lee, Samira Khan, Lavanya Subramanian, Saugata Ghose, Rachata Ausavarungnirun, Gennady Pekhimenko, Vivek Seshadri, and Onur Mutlu, "Design-Induced Latency Variation in Modern DRAM Chips: Characterization, Analysis, and Latency Reduction Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 295: Voltron: Exploiting the Voltage-Latency-Reliability Relationship

## Slide 296: Executive Summary
DRAM (memory) power is significant in today’s systems
  Existing low-voltage DRAM reduces voltage conservatively
Goal: Understand and exploit the reliability and latency behavior of real DRAM chips under aggressive reduced-voltage operation
Key experimental observations:
  Huge voltage margin -- Errors occur beyond some voltage
  Errors exhibit spatial locality
  Higher operation latency mitigates voltage-induced errors
Voltron: A new DRAM energy reduction mechanism
  Reduce DRAM voltage without introducing errors
  Use a regression model to select voltage that does not degrade performance beyond a chosen target  7.3% system energy reduction

## Slide 297: Analysis of Latency-Voltage in DRAM Chips
Kevin Chang, A. Giray Yaglikci, Saugata Ghose, Aditya Agrawal, Niladrish Chatterjee, Abhijith Kashyap, Donghyuk Lee, Mike O'Connor, Hasan Hassan, and Onur Mutlu, "Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 298: And, What If …
… we can sacrifice reliability of some data to access it with even lower latency?

## Slide 299: The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern Commodity DRAM Devices
Jeremie S. Kim Minesh Patel
Hasan Hassan Onur Mutlu
Notes: Hello, my name is Jeremie Kim and I will be talking about the DRAM Latency PUF.

## Slide 300: Motivation
A PUF is function that generates a signature unique to a given device
Used in a Challenge-Response Protocol
  Each device generates a unique PUF response depending the inputs
  A trusted server authenticates a device if it generates the expected PUF response
Notes: [CLICK] A PUF is a function that generates a signature that is unique to a given device. [CLICK] PUFs are often used in a challenge-response protocol where [CLICK] a trusted server issues a set of input parameters to a device, and the device generates the PUF response depending on the input parameters. [CLICK] The trusted server then receives the PUF response and can authenticate the device.

## Slide 301: DRAM Latency Characterization of 223 LPDDR4 DRAM Devices
Latency failures come from accessing DRAM with reduced timing parameters.
Key Observations:
  A cell’s latency failure probability is determined by random process variation
  Latency failure patterns are repeatable and unique to a device
Notes: In this work, we show results from a detailed experimental characterization of 223 state-of-the-art LPDDR4 DRAM devices. [CLICK] We characterize DRAM latency by observing the effects of accessing DRAM with DRAM timing parameters reduced below manufacturer-recommended values.
[CLICK] We make two key observations. [CLICK] first, a cell’s probability to fail, when accessed with reduced timing parameters, is directly correlated with random variations that arise from process manufacturing. [CLICK] secondly, We note that these error patterns from inducing DRAM latency errors are unique to a device and highly repeatable.

## Slide 302: DRAM Latency PUF Key Idea
Row Decoder
High % chance to fail with reduced tRCD
Low % chance to fail with reduced tRCD
SA
SA
SA
SA
SA
SA
SA
Notes: Here is a cartoon showing the manufacturing variation across a region of DRAM. When accessed with a reduced timing parameter, [CLICK] some cells have a high percentage chance of failing, while others [CLICK] have a low percentage chance of failing.

## Slide 303: DRAM Accesses and Failures
wordline
capacitor
access
transistor
bitline
SA
Vdd
0.5 Vdd
Bitline Voltage
Time
Ready to Access
Voltage Level
tRCD
Process variation during manufacturing leads to cells having unique characteristics
Vmin
ACTIVATE
SA Enable
READ
Bitline Charge Sharing
Notes: [CLICK] A DRAM cell holds its charge in a capacitor and gets read out by the sense amplifier via the bitline. [CLICK][CLICK] Initially the bitline is kept at Vdd/2. [CLICK] When the wordline is driven high or activated, [CLICK] the capacitor begins to share charge with the bitline. The sense amplifier is then enabled and [CLICK] the voltage differential on the bitline is amplified to an I/O readable value. [CLICK] In order to ensure correctness of operation, the memory controller can only read data tRCD time after the activation. [CLICK] We could read this data earlier, when it reaches a readable voltage threshold, [CLICK] but other cells, that are weaker due to process variation, might fail. [CLICK]

## Slide 304: DRAM Accesses and Failures
wordline
capacitor
access
transistor
bitline
SA
Vdd
0.5 Vdd
Bitline Voltage
Time
Ready to Access
Voltage Level
tRCD
Vmin
ACTIVATE
SA Enable
READ
weaker cells have a higher probability to fail
Notes: Our method of inducing latency errors is to [CLICK] reduce tRCD below manufacturer-recommended values. Cells that are read when their bitline’s voltage is lower than the threshold, have a probability of failure. This probability increases as you read further below the voltage threshold.

## Slide 305: The DRAM Latency PUF Evaluation
We generate PUF responses using latency errors in a region of DRAM
The latency error patterns satisfy PUF requirements
The DRAM Latency PUF generates PUF responses in 88.2ms
Notes: [CLICK] The DRAM latency PUF generates a PUF response by inducing latency errors in a region of DRAM. [CLICK] We find that the error patterns from latency errors in a DRAM region satisfy the requirements for an effective PUF quite well. [CLICK] The DRAM latency PUF can generate a PUF response in 88.2ms.

## Slide 306: Results
We are orders of magnitude faster than prior DRAM PUFs!
Notes: [CLICK] We show by direct comparison that this is orders of magnitudes faster than the previous best DRAM PUF.

## Slide 307: The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern Commodity DRAM Devices
Jeremie S. Kim Minesh Patel
Hasan Hassan Onur Mutlu
QR Code for the paper
https://people.inf.ethz.ch/omutlu/pub/dram-latency-puf_hpca18.pdf
HPCA 2018
Notes: Please come to my talk at HPCA 2018, if you would like to learn more or have any questions. Thank you very much.

## Slide 308: DRAM Latency PUFs
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 309: Tiered Latency DRAM

## Slide 310: What Causes the Long Latency?
DRAM Latency = Subarray Latency + I/O Latency
DRAM Chip
channel
cell array
I/O
DRAM Chip
channel
I/O
subarray
DRAM Latency = Subarray Latency + I/O Latency
Dominant
Subarray
I/O
Notes: To understand what causes the long latency, let me take a look at the DRAM organization.
DRAM consists of two components, the cell array and the I/O circuitry. The cell array consists of multiple subarrays.
To read from a DRAM chip, the data is first accessed from the subarray and then the data is transferred over the channel by the I/O circuitry.
So, the DRAM latency is the sum of the subarray latency and the I/O latency.
We observed that the subarray latency is much higher than the I/O latency.
As a result, subarray is the dominant source of the DRAM latency as we explained in the paper.

## Slide 311: Why is the Subarray So Slow?
Subarray
row decoder
sense amplifier
capacitor
access
transistor
wordline
bitline
Cell
large sense amplifier
bitline: 512 cells
cell
Long bitline
  Amortizes sense amplifier cost  Small area
  Large bitline capacitance  High latency & power
sense amplifier
row decoder
Notes: The cell’s capacitor is small and can store only a small amount of charge.
That is why a subarray also has sense-amplifiers, which are specialized circuits that can detect the small amount of charge.
Unfortunately, a sense-amplifier size is about *100* times the cell size.
So, to amortize the area of the sense-amplifiers,
hundreds of cells share the same sense-amplifier through a long bitline.
However, a long bitline has a large capacitance that increases latency and power consumption.
Therefore, the long bitline is one of the dominant sources of high latency and high power consumption.
To understand why the subarray is so slow,
let me take a look at the subarray organization.

## Slide 312: Trade-Off: Area (Die Size) vs. Latency
Faster
Smaller
Short Bitline
Long Bitline
Trade-Off: Area vs. Latency
Notes: A naïve way to reduce the DRAM latency is to have short bitlines that have lower latency.
Unfortunately, short bitlines significantly increase the DRAM area.
Therefore, the bitline length exposes an important trade-off between area and latency.

## Slide 313: Trade-Off: Area (Die Size) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.617764350044659 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Commodity DRAM
Long Bitline
Cheaper
Faster
Fancy DRAM
Short Bitline
GOAL
Notes: This figure shows the trade-off between DRAM area and latency as we change the bitline length.
Y-axis is the normalized DRAM area compared to a DRAM using 512 cells/bitline. A lower value is cheaper.
X-axis shows the latency in terms of tRC, an important DRAM timing constraint. A lower value is faster.
Commodity DRAM chips use long bitlines to minimize area cost. On the other hand, shorter bitlines achieve lower latency at higher cost.
Our goal is to achieve the best of both worlds: low latency and low area cost.

## Slide 314: Approximating the Best of Both Worlds
Short Bitline
Low Latency
Long Bitline
Small Area
Long Bitline
Low Latency
Short Bitline
Our Proposal
Small Area
Short Bitline  Fast
Need Isolation
Add Isolation Transistors
High Latency
Large Area
Notes: To sum up, both long and short bitline do not achieve small area and low latency.
Long bitline has small area but has high latency while short bitline has low latency but has large area.
To achieve the best of both worlds, we first start from long bitline, which has small area.
After that, to achieve the low latency of short bitline, we divide the long bitline into two smaller segments.
The bitline length of the segment nearby the sense-amplifier is same as the length of short bitline.
Therefore, the latency of the segment is as low as the latency of the short bitline.
To isolate this fast segment from the other segment, we add isolation transistors that selectively connect the two segments.

## Slide 315: Approximating the Best of Both Worlds
Low Latency
Our Proposal
Small Area
Long Bitline
Small Area
Long Bitline
High Latency
Short Bitline
Low Latency
Short Bitline
Large Area
Tiered-Latency DRAM
Low Latency
Small area using long bitline
Notes: This way, our proposed approach achieves small area and low latency.
We call this new DRAM architecture as Tiered-Latency DRAM

## Slide 316: Commodity DRAM vs. TL-DRAM [HPCA 2013]
Chart: 
| commodity DRAM | near segment | far segment
Normalized Power Consumption | 1 | 0.49 | 1.49
Chart: 
| commodity DRAM | near segment | far segment
Latency | 1 | 0.56 | 1.23
Latency
Power
  –56%
  +23%
  –51%
  +49%
DRAM Latency (tRC)
DRAM Power
DRAM Area Overhead
  ~3%: mainly due to the isolation transistors
  TL-DRAM
  Commodity DRAM
  Near Far
  Commodity DRAM
  Near Far
  TL-DRAM
  (52.5ns)
Notes: This figure compares the latency.
Y-axis is normalized latency.
Compared to commodity DRAM, TL-DRAM’s near segment has 56% lower latency, while the far segment has 23% higher latency.
The right figure compares the power.
Y-axis is normalized power.
Compared to commodity DRAM, TL-DRAM’s near segment has 51% lower power consumption and the far segment has 49% higher power consumption.
Lastly, mainly due to the isolation transistor, Tiered-latency DRAM increases the die-size by about 3%.

## Slide 317: Trade-Off: Area (Die-Area) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.617764350044659 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Cheaper
Faster
Near Segment
Far Segment
GOAL
Notes: Again, the figure shows the trade-off between area and latency in existing DRAM.
Unlike existing DRAM, TL-DRAM achieves low latency using the near segment while increasing the area by only 3%.
Although the far segment has higher latency than commodity DRAM, we show that efficient use of the near segment enables TL-DRAM to achieve high system performance.

## Slide 318: Leveraging Tiered-Latency DRAM
TL-DRAM is a substrate that can be leveraged by the hardware and/or software
Many potential uses
  Use near segment as hardware-managed inclusive cache to far segment
  Use near segment as hardware-managed exclusive cache to far segment
  Profile-based page mapping by operating system
  Simply replace DRAM with TL-DRAM
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: There are multiple ways to leverage the TL-DRAM substrate by hardware or software.
In this slide, I describe many such ways.
First, the near segment can be used as a hardware-managed inclusive cache to the far segment.
Second, the near segment can be used as a hardware-managed exclusive cache to the far segment.
Third, the operating system can intelligently allocate frequently-accessed pages to the near segment.
Forth mechanism is to simple replace DRAM with TL-DRAM without any near segment handling
While our paper provides detailed explanations and evaluations of first three mechanism,
in this talk, we will focus on the first approach, which is to use the near segment as a hardware managed cache for the far segment.

## Slide 319: Performance & Power Consumption
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Performance Improvement | 1.124 | 1.115 | 1.107
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Power Reduction | 0.769 | 0.755 | 0.737
11.5%
Normalized Performance
Core-Count (Channel)
Normalized Power
Core-Count (Channel)
10.7%
12.4%
–23%
–24%
–26%
Using near segment as a cache improves performance and reduces power consumption
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: This figure shows the IPC improvement of our three caching mechanisms over commodity DRAM.
All of them improve performance and benefit-based caching shows maximum performance improvement by 12.7%.
The right figure shows the normalized power reduction of our three caching mechanisms over commodity DRAM.
All of them reduce power consumption and benefit-based caching shows maximum power reduction by 23%.
Therefore, using near segment as a cache improves performance and reduces power consumption at the cost of 3% area overhead.

## Slide 320: Challenge and Opportunity for Future
Fundamentally
Low Latency
Computing Architectures

## Slide 321: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 322: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 323: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 324: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 325: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 326: A Deeper Dive into DRAM Reliability Issues

## Slide 327: There are Two Other Solution Directions
New Technologies: Replace or (more likely) augment DRAM with a different technology
  Non-volatile memories
Embracing Un-reliability:
Design memories with different reliability
and store data intelligently across them
…
Fundamental solutions to security require co-design across the hierarchy
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 328: Exploiting Memory Error Tolerance with Hybrid Memory Systems
Chart: Memory error vulnerability
| App/Data A | App/Data B | App/Data C
System/Application Crash | 1.0414 | 0.63898 | 0.24773
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory [DSN 2014]
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search workload
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 329: More on Heterogeneous-Reliability Memory
Yixin Luo, Sriram Govindan, Bikash Sharma, Mark Santaniello, Justin Meza, Aman Kansal, Jie Liu, Badriddine Khessib, Kushagra Vaid, and Onur Mutlu, "Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost via Heterogeneous-Reliability Memory" Proceedings of the 44th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Atlanta, GA, June 2014. [Summary] [Slides (pptx) (pdf)] [Coverage on ZDNet]

## Slide 330: Root Causes of Disturbance Errors
Cause 1: Electromagnetic coupling
  Toggling the wordline voltage briefly increases the voltage of adjacent wordlines
  Slightly opens adjacent rows  Charge leakage
Cause 2: Conductive bridges
Cause 3: Hot-carrier injection
Confirmed by at least one manufacturer
Notes: Why do the errors occur? We see three possible causes.
First, there could electromagnetic coupling between adjacent wordlines. When the voltage of one is toggled, it could briefly increase the voltage of the other and facilitate the leakage of charge.
Two other possibilities are conductive bridges and hot-carrier injection.
At least one manufacturer confirmed that these three could play a role in the disturbance errors we see them today.

## Slide 331: RowHammer Characterization Results
Most Modules Are at Risk
Errors vs. Vintage
Error = Charge Loss
Adjacency: Aggressor & Victim
Sensitivity Studies
Other Results in Paper
Solution Space
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)
Notes: Now I will present the characterization results, one-by-one.
First, I show that most modules are at risk. Second, I show the number of errors in a module as a function of the manufacture date. Third, I show that the errors are symptomatic of charge loss. Fourth, I show that an aggressor induces errors in adjacent rows. Fifth, I show several sensitivity studies. And, finally, I briefly describe other results in the paper.

## Slide 332: 4. Adjacency: Aggressor & Victim
Most aggressors & victims are adjacent
Note: For three modules with the most errors (only first bank)
Adjacent
Adjacent
Adjacent
Non-Adjacent
Non-Adjacent
Notes: In this figure, the x-axis is the row-address difference between an aggressor and its victims. And the y-axis is the number of victim-aggressor pairs that correspond to the row-address difference. For all three modules, we see strong peaks at plus/minus 1. This implies that aggressors and victims have consecutive row-addresses, in other words, they are adjacent.
However, the figure also shows some victims that are not adjacent to the aggressor. We believe this could be caused by two reasons. First, depending on the mapping, two rows that are physically adjacent within the DRAM chip may not have consecutive row-addresses. Second, fault rows are often re-mapped to spare rows that may reside on a different portion of the DRAM chip.
Nevertheless, we conclude that the vast majority of aggressors & victims are adjacent.

## Slide 333: ❶ Access Interval (Aggressor)
Note: For three modules with the most errors (only first bank)
Not Allowed
Less frequent accesses  Fewer errors
55ns
500ns
Notes: In this figure, the x-axis is the interval at which we access the aggressor. And the y-axis is the number of errors. To comply with the DRAM standard, we employ a default value of 55ns in our experiments. However, as we increase the access-interval, we see that the number of errors decreases. In particular, at 500ns, there are no errors for all three modules.
From this, we conclude that less frequent accesses induce fewer errors.

## Slide 334: ❷ Refresh Interval
Note: Using three modules with the most errors (only first bank)
More frequent refreshes  Fewer errors
~7x frequent
64ms
Notes: In this figure, the x-axis is the refresh-interval. And the y-axis is the number of errors. To comply with the DRAM standard, we employ a default value of 64ms in our experiments. However, as we decrease the refresh-interval, we see that the number of errors decreases. In particular, when the refresh is shortened by 7x, there are no errors for all three modules.
From this, we conclude that more frequent accesses induce fewer errors.

## Slide 335: ❸ Data Pattern
RowStripe
~RowStripe
111111
111111
111111
111111
000000
000000
000000
000000
000000
111111
000000
111111
111111
000000
111111
000000
Solid
~Solid
10x Errors
Errors affected by data stored in other cells
Notes: We tested the modules with four different data-patterns: Solid, inverse Solid, RowStripe, and inverse RowStripe. Solid and inverse Solid give us full coverage since each cell is tested with both 1s and 0s. And the same applies to RowStripe and its inverse.
However, we found that the rowstripe pattern had 10 times as more errors than the solid pattern. We also tested many other data-patterns, including random, but found RowStripe to induce the most errors.
Therefore, we conclude that errors are affected by data stored in other cells due to differences in coupling effects between the cells.

## Slide 336: 6. Other Results (in Paper)
Victim Cells ≠ Weak Cells (i.e., leaky cells)
  Almost no overlap between them
Errors not strongly affected by temperature
  Default temperature: 50°C
  At 30°C and 70°C, number of errors changes <15%
Errors are repeatable
  Across ten iterations of testing, >70% of victim cells had errors in every iteration
Notes: First, we show that victim cells are not weak cells, which are cells that are inherently leaky. According to our experiments, we saw almost no overlap between them.
Second, we show that errors are not strongly affected by temperature. In all of the tests so far, we set the temperature to 50 degrees Celsius. But even when we changed the temperature by 20 degrees, the number of errors changed by less than 15 percent.
Third, we show that errors are repeatable. Across ten iterations of testing, more than 70% of victim cells had errors in every iteration.

## Slide 337: 6. Other Results (in Paper) cont’d
As many as 4 errors per cache-line
  Simple ECC (e.g., SECDED) cannot prevent all errors
Number of cells & rows affected by aggressor
  Victims cells per aggressor: ≤110
  Victims rows per aggressor: ≤9
Cells affected by two aggressors on either side
  Very small fraction of victim cells (<100) have an error when either one of the aggressors is toggled
Notes: Fourth, we show that there are as many as four errors per cacheline. From this, we conclude that simple ECC schemes (for example, SECDED) cannot prevent all errors.
Fifth, we show that the number of cells & rows affected by an aggressor can be as high as 110 or 9, respectively.
Lastly, we show that a very small fraction of victim cells experience an error when either one of the aggressors is toggled.

## Slide 338: Some Potential Solutions
Cost
Make better DRAM chips
Cost, Power
Sophisticated ECC
Power, Performance
Refresh frequently
Cost, Power, Complexity
Access counters
Notes: Here is a list of four potential solutions to disturbance errors: making better DRAM chips, refreshing more frequently, employing sophisticated ECC schemes, and using hardware counters to track the number of accesses to different rows.
However, all of these solutions incur a large overhead in terms cost, power, performance, and/or complexity.

## Slide 339: Naive Solutions
❶ Throttle accesses to same row
  Limit access-interval: ≥500ns
  Limit number of accesses: ≤128K (=64ms/500ns)
❷ Refresh more frequently
  Shorten refresh-interval by ~7x
Both naive solutions introduce significant overhead in performance and power
Notes: Based on what we learned from the sensitivity studies, there are two naive solutions that immediately present themselves.
First, we can throttle accesses to the same row. If the access-interval is greater than 500ns, I showed how errors are not induced. We can achieve the same effect by limiting the maximum number of accesses to the same row to be less than 128K, within a refresh interval.
Second, we can refresh the module more frequently. If the refresh-interval is shortened by 7x, I showed how errors can be prevented.
However, both naive solutions introduce significant overhead in both performance and power. Later on, I will propose a much more efficient solution.

## Slide 340: Apple’s Patch for RowHammer
https://support.apple.com/en-gb/HT204934
HP and Lenovo released similar patches

## Slide 341: Our Solution to RowHammer
PARA: Probabilistic Adjacent Row Activation
Key Idea
  After closing a row, we activate (i.e., refresh) one of its neighbors with a low probability: p = 0.005
Reliability Guarantee
  When p=0.005, errors in one year: 9.4×10-14
  By adjusting the value of p, we can vary the strength of protection against errors
Notes: We provide a more efficient solution, called PARA, which stands for probabilistic adjacent row activation.
The key idea is thus: after closing a row, we activate (i.e., refresh) one of its neighbors with a low probability, for example, p equal to 0.005.
PARA provides a strong reliability guarantee even under the worst-case access patterns to DRAM. When we set p to 0.005, the expected number of errors in one year is 9.4 times 10 to the negative 14. This probability is much lower the failure rate of other hardware components, for example, the hard-disk drive.
And by adjusting the value of p, PARA can provide an arbitrarily strong-degree of protection against errors.

## Slide 342: Advantages of PARA
PARA refreshes rows infrequently
  Low power
  Low performance-overhead
    Average slowdown: 0.20% (for 29 benchmarks)
    Maximum slowdown: 0.75%
PARA is stateless
  Low cost
  Low complexity
PARA is an effective and low-overhead solution to prevent disturbance errors
Notes: PARA has many advantages. Since it refreshes row infrequently, it has low power and low performance-overhead. Simulated across 29 benchmarks, we saw an average of only 0.2% slowdown and a maximum of only 0.75% slowdown.
In addition, due to its stateless nature, PARA has low cost and complexity.
Therefore, PARA is an effective and low-overhead solution to prevent disturbance errors.

## Slide 343: Requirements for PARA
If implemented in DRAM chip
  Enough slack in timing parameters
  Plenty of slack today:
    Lee et al., “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common Case,” HPCA 2015.
    Chang et al., “Understanding Latency Variation in Modern DRAM Chips,” SIGMETRICS 2016.
    Lee et al., “Design-Induced Latency Variation in Modern DRAM Chips,” SIGMETRICS 2017.
    Chang et al., “Understanding Reduced-Voltage Operation in Modern DRAM Devices,” SIGMETRICS 2017.
If implemented in memory controller
  Better coordination between memory controller and DRAM
  Memory controller should know which rows are physically adjacent

## Slide 344: More on RowHammer Analysis
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data]

## Slide 345: Retrospective on RowHammer & Future
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 346: Challenge and Opportunity for Future
Fundamentally
Secure, Reliable, Safe
Computing Architectures

## Slide 347: Future of Main Memory
DRAM is becoming less reliable  more vulnerable

## Slide 348: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 349
Intuition: quadratic increase in capacity
DRAM Reliability Reducing

## Slide 350: Aside: SSD Error Analysis in the Field
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet]

## Slide 351: Future of Main Memory
DRAM is becoming less reliable  more vulnerable
Due to difficulties in DRAM scaling, other problems may also appear (or they may be going unnoticed)
Some errors may already be slipping into the field
  Read disturb errors (Rowhammer)
  Retention errors
  Read errors, write errors
  …
These errors can also pose security vulnerabilities

## Slide 352: DRAM Data Retention Time Failures
Determining the data retention time of a cell/row is getting more difficult
Retention failures may already be slipping into the field

## Slide 353: Analysis of Retention Failures [ISCA’13]
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 354: Two Challenges to Retention Time Profiling
Data Pattern Dependence (DPD) of retention time
Variable Retention Time (VRT) phenomenon

## Slide 355: Two Challenges to Retention Time Profiling
Challenge 1: Data Pattern Dependence (DPD)
  Retention time of a DRAM cell depends on its value and the values of cells nearby it
  When a row is activated, all bitlines are perturbed simultaneously

## Slide 356: Data Pattern Dependence
Electrical noise on the bitline affects reliable sensing of a DRAM cell
The magnitude of this noise is affected by values of nearby cells via
  Bitline-bitline coupling  electrical coupling between adjacent bitlines
  Bitline-wordline coupling  electrical coupling between each bitline and the activated wordline
Notes: If a cell has lost enough charge, this noise can be large enough to cause a failure on a read
(normally, there is enough noise margin to tolerate the coupling noise)

## Slide 357: Data Pattern Dependence
Electrical noise on the bitline affects reliable sensing of a DRAM cell
The magnitude of this noise is affected by values of nearby cells via
  Bitline-bitline coupling  electrical coupling between adjacent bitlines
  Bitline-wordline coupling  electrical coupling between each bitline and the activated wordline
Retention time of a cell depends on data patterns stored in nearby cells
 need to find the worst data pattern to find worst-case retention time
 this pattern is location dependent
Notes: If a cell has lost enough charge, this noise can be large enough to cause a failure on a read
(normally, there is enough noise margin to tolerate the coupling noise)

## Slide 358: Two Challenges to Retention Time Profiling
Challenge 2: Variable Retention Time (VRT)
  Retention time of a DRAM cell changes randomly over time
    a cell alternates between multiple retention time states
  Leakage current of a cell changes sporadically due to a charge trap in the gate oxide of the DRAM cell access transistor
  When the trap becomes occupied, charge leaks more readily from the transistor’s drain, leading to a short retention time
    Called Trap-Assisted Gate-Induced Drain Leakage
  This process appears to be a random process [Kim+ IEEE TED’11]
  Worst-case retention time depends on a random process
     need to find the worst case despite this

## Slide 359: Modern DRAM Retention Time Distribution
Newer device families have more weak cells than older ones
Likely a result of technology scaling
OLDER
NEWER
OLDER
NEWER

## Slide 360: An Example VRT Cell
A cell from E 2Gb chip family

## Slide 361: Variable Retention Time
A 2Gb chip family
Min ret time = Max ret time
Expected if no VRT
Most failing cells
exhibit VRT
Many failing cells jump from
very high retention time to very low

## Slide 362: More on DRAM Retention Analysis
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 363: Industry Is Writing Papers About It, Too

## Slide 364: Industry Is Writing Papers About It, Too

## Slide 365: Mitigation of Retention Issues [SIGMETRICS’14]
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 366: Handling Data-Dependent Failures [DSN’16]
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 367: Handling Data-Dependent Failures [CAL’16]
Samira Khan, Chris Wilkerson, Donghyuk Lee, Alaa R. Alameldeen, and Onur Mutlu, "A Case for Memory Content-Based Detection and Mitigation of Data-Dependent Failures in DRAM" IEEE Computer Architecture Letters (CAL), November 2016.

## Slide 368: Handling Variable Retention Time [DSN’15]
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 369: Handling Both DPD and VRT [ISCA’17]
Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "The Reach Profiler (REAPER): Enabling the Mitigation of DRAM Retention Failures via Profiling at Aggressive Conditions" Proceedings of the 44th International Symposium on Computer Architecture (ISCA), Toronto, Canada, June 2017.
First experimental analysis of (mobile) LPDDR4 chips
Analyzes the complex tradeoff space of retention time profiling
Key idea: enable fast and robust profiling at higher refresh intervals & temp.

## Slide 370: Summary: Memory Reliability and Security
Memory reliability is reducing
Reliability issues open up security vulnerabilities
  Very hard to defend against
Rowhammer is an example
  Its implications on system security research are tremendous & exciting
Good news: We have a lot more to do.
Understand: Solid methodologies for failure modeling and discovery
  Modeling based on real device data – small scale and large scale
Architect: Principled co-architecting of system and memory
  Good partitioning of duties across the stack
Design & Test: Principled electronic design, automation, testing
  High coverage and good interaction with system reliability methods

## Slide 371: If Time Permits: NAND Flash Vulnerabilities
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" to appear in Proceedings of the IEEE, 2017.
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.
Fukami+, “Improving the Reliability of Chip-Off Forensic Analysis of NAND Flash Memory Devices,” DFRWS EU 2017.
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 372: Overview Paper on Flash Reliability
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" to appear in Proceedings of the IEEE, 2017.

## Slide 373: Challenge and Opportunity for Future
Fundamentally
Secure, Reliable, Safe
Computing Architectures

## Slide 374: NAND Flash Memory Reliability and Security

## Slide 375: Upcoming Overview Paper
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" to appear in Proceedings of the IEEE, 2017.

## Slide 376: Evolution of NAND Flash Memory
Flash memory is widening its range of applications
  Portable consumer devices, laptop PCs and enterprise servers
Seaung Suk Lee, “Emerging Challenges in NAND Flash Technology”, Flash Summit 2011 (Hynix)
CMOS scaling
More bits per Cell

## Slide 377: Flash Challenges: Reliability and Endurance
E. Grochowski et al., “Future technology challenges for NAND flash and HDD products”, Flash Memory Summit 2012
P/E cycles (required)
P/E cycles (provided)
A few thousand
Writing
the full capacity
of the drive
10 times per day
for 5 years
(STEC)
> 50k P/E cycles

## Slide 378: NAND Flash Memory is Increasingly Noisy
Noisy NAND
Write
Read

## Slide 379: Future NAND Flash-based Storage Architecture
Memory
Signal
Processing
Error
Correction
Raw Bit
Error Rate
Uncorrectable
BER < 10-15
Noisy
High
Lower
Build reliable error models for NAND flash memory
Design efficient reliability mechanisms based on the model
Our Goals:
Better

## Slide 380: NAND Flash Error Model
Noisy NAND
Write
Read
Experimentally characterize and model dominant errors
Neighbor page prog/read (c-to-c interference)
Retention
Erase block
Program page
Write
Read
Cai et al., “Threshold voltage distribution in MLC NAND Flash Memory: Characterization, Analysis, and Modeling”, DATE 2013
Cai et al., “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques”, HPCA 2017
Cai et al., “Flash Correct-and-Refresh: Retention-aware error management for increased flash memory lifetime”, ICCD 2012
Cai et al., “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation”, ICCD 2013
Cai et al., “Neighbor-Cell Assisted Error Correction in MLC NAND Flash Memories”, SIGMETRICS 2014
Cai et al., “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation”, DSN 2015
Cai et al., “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis””, DATE 2012
Cai et al., “Error Analysis and Retention-Aware Error Management for NAND Flash Memory, ITJ 2013
Cai et al., “Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" , HPCA 2015
Luo et al., “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory”, JSAC 2016

## Slide 381: Our Goals and Approach
Goals:
  Understand error mechanisms and develop reliable predictive models for MLC NAND flash memory errors
  Develop efficient error management techniques to mitigate errors and improve flash reliability and endurance
Approach:
  Solid experimental analyses of errors in real MLC NAND flash memory  drive the understanding and models
  Understanding, models, and creativity  drive the new techniques

## Slide 382: Experimental Testing Platform
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017]
Cai et al., FPGA-based Solid-State Drive prototyping platform, FCCM 2011.

## Slide 383: NAND Flash Error Types
Four types of errors [Cai+, DATE 2012]
Caused by common flash operations
  Read errors
  Erase errors
  Program (interference) errors
Caused by flash cell losing charge over time
  Retention errors
    Whether an error happens depends on required retention time
    Especially problematic in MLC flash because threshold voltage window to determine stored value is smaller

## Slide 384: Observations: Flash Error Analysis
retention errors
Raw bit error rate increases exponentially with P/E cycles
Retention errors are dominant (>99% for 1-year ret. time)
Retention errors increase with retention time requirement
P/E Cycles
Raw Bit Error Rate
Cai et al., Error Patterns in MLC NAND Flash Memory, DATE 2012.

## Slide 385: More on Flash Error Analysis
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Dresden, Germany, March 2012. Slides (ppt)

## Slide 386: Solution to Retention Errors
Refresh periodically
Change the period based on P/E cycle wearout
  Refresh more often at higher P/E cycles
Use a combination of in-place and remapping-based refresh

## Slide 387: One Issue: Read Disturb in Flash Memory
All scaled memories are prone to read disturb errors

## Slide 388: NAND Flash Memory Background
Flash Memory
Page 1
Page 0
Page 2
Page 255
……
Page 257
Page 256
Page 258
Page 511
……
……
Page M+1
Page M
Page M+2
Page M+255
……
Flash Controller
Block 0
Block 1
Block N
Read
Pass
Pass
…
Pass
Notes: When we read from one page in a block, we apply a high voltage to all the other pages in the same block. We will explain why later

## Slide 389: Flash Cell Array
Sense Amplifiers
Block X
Page Y
Sense Amplifiers
Row
Column
Notes: Now, let’s zoom in to a single block of flash memory, which consists of an array of flash pages.
Each flash page is written to flash cells located in the same row.
Each row of cells are controlled by the same horizontal wire.
Each column of cells are connected in series with a sense amplifier at the bottom.

## Slide 390: Flash Cell
Floating Gate
Gate
Drain
Source
Floating Gate Transistor
(Flash Cell)
Vth = 2.5 V
Notes: Now let’s zoom in again to look at a single flash cell, or, it can also be called, a floating gate transistor.

## Slide 391: Flash Read
Vread = 2.5 V
Vth = 3 V
Vth = 2 V
1
0
Vread = 2.5 V
Gate
Notes: Now, if we have two flash cells programmed to different threshold voltages, 2V and 3V, we can distinguish them with a read voltage of 2.5V.
When we apply 2.5V to the gate, since the read voltage is higher than the threshold voltage, …
Now if we look back at this example, we can see that the threshold voltage of each flash cell actually represents the value being stored.

## Slide 392: Flash Pass-Through
Vpass = 5 V
Vth = 2 V
1
Vpass = 5 V
Gate
1
Vth = 3 V
Notes: But, for the same cells, when we apply a high voltage to them, regardless of the threshold voltage, any cell will be passed-through.
So we call this voltage pass-through voltage or Vpass

## Slide 393: Read from Flash Cell Array
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.4V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Vread = 2.5 V
Vpass = 5.0 V
Vpass = 5.0 V
Vpass = 5.0 V
1
1
0
0
Correct values for page 2:
Page 1
Page 2
Page 3
Page 4
Pass (5V)
Read (2.5V)
Pass (5V)
Pass (5V)
Notes: Now, let’s look at an example array of flash cells.
In this example, we make up threshold voltage numbers for each cell.
Let’s say we want to read from the second page in this array.
So we apply a read voltage of 2.5 V to the second page
And since all the other pages are connected in series, we apply a high pass-through voltage of 5 V to the other pages.
As we can see, the high pass through voltage switches on all the flash pages being passed-through, allowing the sense amplifier to read the values stored in the second page.
In this case, the correct values …

## Slide 394: Read Disturb Problem: “Weak Programming” Effect
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.4V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Repeatedly read page 3 (or any page other than page 2)
Read (2.5V)
Pass (5V)
Pass (5V)
Pass (5V)
Page 1
Page 2
Page 3
Page 4
Notes: However, the high pass through voltage can generate read disturb problem, which we will introduce now.
When we want to read page 3, instead of page 2, this high pass through voltage now needs to be applied on the 2nd page.
When we repeatedly read page 3, the pass through voltage induces a weak programming effect on the second page.

## Slide 395: Read Disturb Problem: “Weak Programming” Effect
Vread = 2.5 V
Vpass = 5.0 V
Vpass = 5.0 V
Vpass = 5.0 V
0
1
0
0
High pass-through voltage induces “weak-programming” effect
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Incorrect values from page 2:
2.4V
2.6V
Page 1
Page 2
Page 3
Page 4
Notes: As the weak programming effect accumulates, the threshold voltage of each flash cell increases, and the threshold voltage state of a cell can be altered.
In this case, when we read page 2 again, we will read incorrect values from page 2, 0001
Flash vendors conservatively set this pass-through voltage to a high voltage.
However, we find in the paper that it is unnecessary to set to this high, and that reducing this voltage by just a bit will reduce read disturb errors significantly in the future.

## Slide 396: Executive Summary
Read disturb errors limit flash memory lifetime today
  Apply a high pass-through voltage (Vpass) to multiple pages on a read
  Repeated application of Vpass can alter stored values in unread pages
We characterize read disturb on real NAND flash chips
  Slightly lowering Vpass greatly reduces read disturb errors
  Some flash cells are more prone to read disturb
Technique 1: Mitigate read disturb errors online
  Vpass Tuning dynamically finds and applies a lowered Vpass per block
  Flash memory lifetime improves by 21%
Technique 2: Recover after failure to prevent data loss
  Read Disturb Oriented Error Recovery (RDR) selectively corrects cells more susceptible to read disturb errors
  Reduces raw bit error rate (RBER) by up to 36%
Notes: When we read data from one page, we have to apply a high voltage to multiple other flash pages that are connected to this page, and we call this high pass-through voltage.
Over time this high pass-through voltage can alter the values stored in unread flash pages. We call this a read disturb error.
For the first time in open literature, we characterize read disturb on real NAND flash chips, and show that read disturb errors exist in today’s flash chips and is expected to increase in the future.
We make two key observations from the characterization.
Using our characterization, we develop two techniques that can help flash memory tolerate such read disturb errors.

## Slide 397: More on Flash Read Disturb Errors
Yu Cai, Yixin Luo, Saugata Ghose, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015.

## Slide 398: Large-Scale Flash SSD Error Analysis
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet] [Coverage on The Register] [Coverage on TechSpot] [Coverage on The Tech Report]

## Slide 399: Another Time: NAND Flash Vulnerabilities
Onur Mutlu, "Error Analysis and Management for MLC NAND Flash Memory" Technical talk at Flash Memory Summit 2014 (FMS), Santa Clara, CA, August 2014. Slides (ppt) (pdf)
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.
Fukami+, “Improving the Reliability of Chip-Off Forensic Analysis of NAND Flash Memory Devices,” DFRWS EU 2017.

## Slide 400: Flash Memory Programming Vulnerabilities
Yu Cai, Saugata Ghose, Yixin Luo, Ken Mai, Onur Mutlu, and Erich F. Haratsch, "Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques" Proceedings of the 23rd International Symposium on High-Performance Computer Architecture (HPCA) Industrial Session, Austin, TX, USA, February 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 401: Other Works on Flash Memory

## Slide 402: NAND Flash Error Model
Noisy NAND
Write
Read
Experimentally characterize and model dominant errors
Neighbor page prog/read (c-to-c interference)
Retention
Erase block
Program page
Write
Read
Cai et al., “Threshold voltage distribution in MLC NAND Flash Memory: Characterization, Analysis, and Modeling”, DATE 2013
Cai et al., “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques”, HPCA 2017
Cai et al., “Flash Correct-and-Refresh: Retention-aware error management for increased flash memory lifetime”, ICCD 2012
Cai et al., “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation”, ICCD 2013
Cai et al., “Neighbor-Cell Assisted Error Correction in MLC NAND Flash Memories”, SIGMETRICS 2014
Cai et al., “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation”, DSN 2015
Cai et al., “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis””, DATE 2012
Cai et al., “Error Analysis and Retention-Aware Error Management for NAND Flash Memory, ITJ 2013
Cai et al., “Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" , HPCA 2015
Luo et al., “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory”, JSAC 2016

## Slide 403: Threshold Voltage Distribution
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Grenoble, France, March 2013. Slides (ppt)

## Slide 404: Program Interference and Vref Prediction
Yu Cai, Onur Mutlu, Erich F. Haratsch, and Ken Mai, "Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation" Proceedings of the 31st IEEE International Conference on Computer Design (ICCD), Asheville, NC, October 2013. Slides (pptx) (pdf) Lightning Session Slides (pdf)

## Slide 405: Neighbor-Assisted Error Correction
Yu Cai, Gulay Yalcin, Onur Mutlu, Eric Haratsch, Osman Unsal, Adrian Cristal, and Ken Mai, "Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. Slides (ppt) (pdf)

## Slide 406: Data Retention
Yu Cai, Yixin Luo, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)]

## Slide 407: SSD Error Analysis in the Field
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet] [Coverage on The Register] [Coverage on TechSpot] [Coverage on The Tech Report]

## Slide 408: Flash Memory Programming Vulnerabilities
Yu Cai, Saugata Ghose, Yixin Luo, Ken Mai, Onur Mutlu, and Erich F. Haratsch, "Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques" Proceedings of the 23rd International Symposium on High-Performance Computer Architecture (HPCA) Industrial Session, Austin, TX, USA, February 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 409: Accurate and Online Channel Modeling
Yixin Luo, Saugata Ghose, Yu Cai, Erich F. Haratsch, and Onur Mutlu, "Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory" to appear in IEEE Journal on Selected Areas in Communications (JSAC), 2016.

## Slide 410: More on DRAM Refresh

## Slide 411: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 412: Summary: Refresh-Access Parallelization
DRAM refresh interferes with memory accesses
  Degrades system performance and energy efficiency
  Becomes exacerbated as DRAM density increases
Goal: Serve memory accesses in parallel with refreshes to reduce refresh interference on demand requests
Our mechanisms:
  1. Enable more parallelization between refreshes and accesses across different banks with new per-bank refresh scheduling algorithms
  2. Enable serving accesses concurrently with refreshes in the same bank by exploiting parallelism across DRAM subarrays
Improve system performance and energy efficiency for a wide variety of different workloads and DRAM densities
  20.2% and 9.0% for 8-core systems using 32Gb DRAM at low cost
  Very close to the ideal scheme without refreshes
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.

## Slide 413: Refresh Penalty
Processor
Memory Controller
DRAM
Refresh
Read
Data
Capacitor
Access transistor
Refresh delays requests by 100s of ns
Refresh interferes with memory accesses

## Slide 414: Existing Refresh Modes
Time
Per-bank refresh in mobile DRAM (LPDDRx)
Time
All-bank refresh in commodity DRAM (DDRx)
Bank 7
Bank 1
Bank 0
…
Bank 7
Bank 1
Bank 0
…
Refresh
Round-robin order
…
Per-bank refresh allows accesses to other banks while a bank is refreshing

## Slide 415: Shortcomings of Per-Bank Refresh
Problem 1: Refreshes to different banks are scheduled in a strict round-robin order
  The static ordering is hardwired into DRAM chips
  Refreshes busy banks with many queued requests when other banks are idle
Key idea: Schedule per-bank refreshes to idle banks opportunistically in a dynamic order

## Slide 416: Our First Approach: DARP
Dynamic Access-Refresh Parallelization (DARP)
  An improved scheduling policy for per-bank refreshes
  Exploits refresh scheduling flexibility in DDR DRAM
Component 1: Out-of-order per-bank refresh
  Avoids poor static scheduling decisions
  Dynamically issues per-bank refreshes to idle banks
Component 2: Write-Refresh Parallelization
  Avoids refresh interference on latency-critical reads
  Parallelizes refreshes with a batch of writes

## Slide 417: Shortcomings of Per-Bank Refresh
Problem 2: Banks that are being refreshed cannot concurrently serve memory requests
Time
Bank 0
RD
Delayed by refresh
Per-Bank Refresh

## Slide 418: Shortcomings of Per-Bank Refresh
Problem 2: Refreshing banks cannot concurrently serve memory requests
Key idea: Exploit subarrays within a bank to parallelize refreshes and accesses across subarrays
Time
Bank 0
Subarray 1
Subarray 0
RD
Subarray Refresh
Time
Parallelize

## Slide 419: Methodology
100 workloads: SPEC CPU2006, STREAM, TPC-C/H, random access
System performance metric: Weighted speedup
DDR3 Rank
Simulator configurations
Memory Controller
8-core processor
Memory Controller
Bank 7
Bank 1
Bank 0
…
L1 $: 32KB
L2 $: 512KB/core

## Slide 420: Comparison Points
All-bank refresh [DDR3, LPDDR3, …]
Per-bank refresh [LPDDR3]
Elastic refresh [Stuecheli et al., MICRO ‘10]:
  Postpones refreshes by a time delay based on the predicted rank idle time to avoid interference on memory requests
  Proposed to schedule all-bank refreshes without exploiting per-bank refreshes
  Cannot parallelize refreshes and accesses within a rank
Ideal (no refresh)

## Slide 421: System Performance
Chart: DRAM Chip Density
All-Bank | 5.5359 | 5.3024 | 4.8311
Per-Bank | 5.7551 | 5.5256 | 5.0271
Elastic | 5.6343 | 5.3803 | 4.8911
DARP | 5.9537 | 5.8162 | 5.2317
SARP | 5.9777 | 5.9152 | 5.7295
DSARP | 5.9723 | 5.9543 | 5.8059
Ideal | 6.0252 | 6.0252 | 6.0252
7.9%
12.3%
20.2%
1. Both DARP & SARP provide performance gains and combining them (DSARP) improves even more
2. Consistent system performance improvement across DRAM densities (within 0.9%, 1.2%, and 3.8% of ideal)

## Slide 422: Energy Efficiency
3.0%
5.2%
9.0%
Consistent reduction on energy consumption
Chart: DRAM Chip Density
All-Bank | 38.2974 | 40.28 | 44.8967
Per-Bank | 38.0134 | 39.9893 | 44.5521
Elastic | 37.5049 | 39.3169 | 44.1509
DARP | 37.191 | 38.5881 | 43.25
SARP | 37.1096 | 38.322 | 41.0809
DSARP | 37.137 | 38.197 | 40.8495
Ideal | 36.6284 | 36.6284 | 36.6284

## Slide 423: More Information on Refresh-Access Parallelization
Kevin Chang, Donghyuk Lee, Zeshan Chishti, Alaa Alameldeen, Chris Wilkerson, Yoongu Kim, and Onur Mutlu, "Improving DRAM Performance by Parallelizing Refreshes with Accesses" Proceedings of the 20th International Symposium on High-Performance Computer Architecture (HPCA), Orlando, FL, February 2014. [Summary] [Slides (pptx) (pdf)]

## Slide 424: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 425: Most Refreshes Are Unnecessary
Retention Time Profile of DRAM looks like this:

## Slide 426: RAIDR: Eliminating Unnecessary Refreshes
1. Profiling: Profile the retention time of all DRAM rows
2. Binning: Store rows into bins by retention time
 use Bloom Filters for efficient and scalable storage
3. Refreshing: Memory controller refreshes rows in different bins at different rates
 probe Bloom Filters to determine refresh rate of a row
1.25KB storage in controller for 32GB DRAM memory
Can reduce refreshes by ~75%
 reduces energy consumption and improves performance
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 427: RAIDR: Baseline Design
Refresh control is in DRAM in today’s auto-refresh systems
RAIDR can be implemented in either the controller or DRAM

## Slide 428: RAIDR in Memory Controller: Option 1
Overhead of RAIDR in DRAM controller:
1.25 KB Bloom Filters, 3 counters, additional commands issued for per-row refresh (all accounted for in evaluations)

## Slide 429: RAIDR in DRAM Chip: Option 2
Overhead of RAIDR in DRAM chip:
Per-chip overhead: 20B Bloom Filters, 1 counter (4 Gbit chip)
Total overhead: 1.25KB Bloom Filters, 64 counters (32 GB DRAM)

## Slide 430: RAIDR: Results and Takeaways
System: 32GB DRAM, 8-core; SPEC, TPC-C, TPC-H workloads
RAIDR hardware cost: 1.25 kB (2 Bloom filters)
Refresh reduction: 74.6%
Dynamic DRAM energy reduction: 16%
Idle DRAM power reduction: 20%
Performance improvement: 9%
Benefits increase as DRAM scales in density

## Slide 431: DRAM Device Capacity Scaling: Performance
RAIDR performance benefits increase with DRAM chip capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 432: DRAM Device Capacity Scaling: Energy
RAIDR energy benefits increase with DRAM chip capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 433: RAIDR: Eliminating Unnecessary Refreshes
Observation: Most DRAM rows can be refreshed much less often without losing data [Kim+, EDL’09][Liu+ ISCA’13]
Key idea: Refresh rows containing weak cells
more frequently, other rows less frequently
  1. Profiling: Profile retention time of all rows
  2. Binning: Store rows into bins by retention time in memory controller
  Efficient storage with Bloom Filters (only 1.25KB for 32GB memory)
  3. Refreshing: Memory controller refreshes rows in different bins at different rates
Results: 8-core, 32GB, SPEC, TPC-C, TPC-H
  74.6% refresh reduction @ 1.25KB storage
  ~16%/20% DRAM dynamic/idle power reduction
  ~9% performance improvement
  Benefits increase with DRAM capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 434: More on RAIDR
Jamie Liu, Ben Jaiyen, Richard Veras, and Onur Mutlu, "RAIDR: Retention-Aware Intelligent DRAM Refresh" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pdf)

## Slide 435: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 436: Motivation: Understanding Retention
Past works require accurate and reliable measurement of retention time of each DRAM row
  To maintain data integrity while reducing refreshes
Assumption: worst-case retention time of each row can be determined and stays the same at a given temperature
  Some works propose writing all 1’s and 0’s to a row, and measuring the time before data corruption
Question:
  Can we reliably and accurately determine retention times of all DRAM rows?

## Slide 437: Two Challenges to Retention Time Profiling
Data Pattern Dependence (DPD) of retention time
Variable Retention Time (VRT) phenomenon

## Slide 438: An Example VRT Cell
A cell from E 2Gb chip family

## Slide 439: VRT: Implications on Profiling Mechanisms
Problem 1: There does not seem to be a way of determining if a cell exhibits VRT without actually observing a cell exhibiting VRT
  VRT is a memoryless random process [Kim+ JJAP 2010]
Problem 2: VRT complicates retention time profiling by DRAM manufacturers
  Exposure to very high temperatures can induce VRT in cells that were not previously susceptible
   can happen during soldering of DRAM chips
   manufacturer’s retention time profile may not be accurate
One option for future work: Use ECC to continuously profile DRAM online while aggressively reducing refresh rate
  Need to keep ECC overhead in check

## Slide 440: More on DRAM Retention Analysis
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 441: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 442: Towards an Online Profiling System
Key Observations:
Testing alone cannot detect all possible failures
Combination of ECC and other mitigation techniques is much more effective
  But degrades performance
Testing can help to reduce the ECC strength
  Even when starting with a higher strength ECC
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Notes: Our high-level design for online profiling system is based to thee key observations:

## Slide 443: Towards an Online Profiling System
Run tests periodically after a short interval
at smaller regions of memory
Initially Protect DRAM
with Strong ECC
1
Periodically Test
Parts of DRAM
2
ECC
Test
Test
Test
Mitigate errors and
reduce ECC
3
Notes: Based on these observations, we propose that in an online profiling system,

## Slide 444: More on Online Profiling of DRAM
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 445: How Do We Make RAIDR Work in the Presence of the VRT Phenomenon?

## Slide 446: Making RAIDR Work w/ Online Profiling & ECC
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 447: AVATAR
Insight: Avoid retention failures  Upgrade row on ECC error
Observation: Rate of VRT >> Rate of soft error (50x-2500x)
A
B
C
D
E
F
G
H
DRAM Rows
RETENTION
PROFILING
Weak Cell
0
0
1
0
0
0
1
0
Ref. Rate Table
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
1
AVATAR mitigates VRT by increasing refresh rate on error
Scrub
(15 min)
Row protected from future
retention failures

## Slide 448: RESULTS: REFRESH SAVINGS
AVATAR
No VRT
AVATAR reduces refresh by 60%-70%, similar to multi rate refresh but with VRT tolerance
Retention Testing Once a Year can revert refresh saving from 60% to 70%

## Slide 449: SPEEDUP
Speedup
Chart: 
| 8Gb | 16Gb | 32Gb | 64Gb
AVATAR (1yr) | 1.04 | 1.065 | 1.13 | 1.35
NoRefresh | 1.05 | 1.09 | 1.21 | 1.54
AVATAR gets 2/3rd the performance of NoRefresh. More gains at higher capacity nodes

## Slide 450: ENERGY DELAY PRODUCT
Chart: 
| 8Gb | 16Gb | 32Gb | 64Gb
AVATAR (1yr) | 0.95 | 0.88 | 0.75 | 0.52
NoRefresh | 0.91 | 0.83 | 0.68 | 0.41
Energy Delay Product
AVATAR reduces EDP,
Significant reduction at higher capacity nodes

## Slide 451: Making RAIDR Work w/ Online Profiling & ECC
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 452: DRAM Refresh: Summary and Conclusions
DRAM refresh is a critical challenge
  in scaling DRAM technology efficiently to higher capacities
Discussed several promising solution directions
  Parallelize refreshes with accesses [Chang+ HPCA’14]
  Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Examined properties of retention time behavior [Liu+ ISCA’13]
  Enable realistic VRT-Aware refresh techniques [Qureshi+ DSN’15]
Many avenues for overcoming DRAM refresh challenges
  Handling DPD/VRT phenomena
  Enabling online retention time profiling and error mitigation
  Exploiting application behavior

## Slide 453: Other Backup Slides

## Slide 454: Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Amirali Boroumand
Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun,
Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu

## Slide 455: Consumer Devices
Consumer devices are everywhere!
Energy consumption is a first-class concern in consumer devices
Notes: Consumer devices like tablets smartphone and wearable are now everywhere and used by billions of people.
One of the major challenge in these devices is battery limitation which makes the energy consumption a critical concern …

## Slide 456: Popular Google Consumer Workloads
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 457: Energy Cost of Data Movement
Data Movement
1st key observation: 62.7% of the total system energy is spent on data movement
  Potential solution: move computation close to data
  Challenge: limited area and energy budget
Processing-in-Memory (PIM)
SoC
DRAM
L2
L1
CPU
CPU
CPU
CPU
Compute Unit
Notes: Throughout our analysis, we make a key observation that out of all sources of energy consumption, data movement is a major contributor to the total system energy. We find that across all of the workloads, on average around 62.7% of total system energy is spent on data movement.
One way to reduce data movement cost is to move computation close to data, or …
One potential solution to address this cost it do move computation close to data, or in other words, do procesing in memory. However, the challenge is that these devices.
One potential solution to mitigate data movement cost and reduce total system energy is to execute data-movement heavy portions of application close to data, or in other words, do processing in memory. However, consumer devices are extermely limited in terms of area and power budget. So the question is can we move part of the data movement heavy portion given the limited area and energy budget. Our

## Slide 458: Using PIM to Reduce Data Movement
  2nd key observation: a significant fraction of data movement often comes from simple functions
PIM Core
PIM Accelerator
PIM Accelerator
PIM Accelerator
We can design lightweight logic to implement these simple functions in memory
Small embedded low-power core
Small fixed-function accelerators
  Offloading to PIM logic reduces energy by 55.4% and improves performance by 54.2% on average
Notes: To figure out if we can use processing in memory, we dig deeper into our analysis and we make another key observation that majority of data movement often comes form simple functions and pritmitives. We find that these simple function can be implemented in memory as either a small embedded core, or group of small fixed function accelerators. Our result shows that offloading these function to PIM logic can significantly reduce data movement for each function and reduce energy on average around 55% and improve perforamcne around 54%.

## Slide 459: Goals
1
2
Understand the data movement related bottlenecks in modern consumer workloads
Analyze opportunities to mitigate data movement by using processing-in-memory (PIM)
    Design PIM logic that can maximize energy efficiency given the limited area and energy budget in consumer devices
3

## Slide 460: Outline
  Introduction
  Background
  Analysis Methodology
  Workload Analysis
  Evaluation
  Conclusion
Notes: Before we jump into our analysis, lets talk about …

## Slide 461: Potential Solution to Address Data Movement
Processing-in-Memory (PIM)
  A potential solution to reduce data movement
  Idea: move computation close to data
Enabled by recent advances in 3D-stacked memory
Reduces data movement
Exploits large in-memory bandwidth
Exploits shorter access latency to memory

## Slide 462: Outline
  Introduction
  Background
  Analysis Methodology
  Workload Analysis
  Evaluation
  Conclusion

## Slide 463: Workload Analysis Methodology
  Workload Characterization
  Chromebook with an Intel Celeron SoC and 2GB of DRAM
  Extensively use performance counters within SoC
Energy Model
  Sum of the energy consumption within the CPU, all caches, off-chip interconnects, and DRAM
DRAM
L2
L1
CPU
CPU
Notes: Feedback: no wifi mention
We did our workload characterization on a Chromebook with an Intel SoC. We use performance counter within Soc to do our analysis.
We model energy as sum of the energy consumption that take place in CPU, caches, interconnet and DRAM. We turn off the wifi and use the lowest brightness for the display to ensure that the majority of the total energy is spent on the SoC and the memory system

## Slide 464: PIM Logic Implementation
SoC
DRAM
Logic Layer
PIM Core
PIM Accelerator
PIM Accelerator
PIM Accelerator N
  Customized embedded general-purpose core
    256-bit SIMD unit
    No aggressive ILP techniques
  Small fixed-function accelerators
    Multiple copies of customized in-memory logic unit
Notes: During our analysis, for each workload, once we identify a PIM target, we consider two types of PIM logic implementation: (1) a general-purpose PIM core; and (2) a fixed-function PIM accelerator,
For the PIM core, we design a small general purpose core based on the charateristic of PIM candidate we find across the workloads. It’s simple embedded core that doesn’t have any aggressi ILP techniques, and it includes a SIMD unit to benefit from parallelism. For the PIM accelerator, we design a fixed function logic that has an in memory logic unit for each candidates we find. To benefit from paralalliesm, eacch PIM accelerator has multiple. ..
that can run any of the PIM candidates we find. Majortiy of the candidates we find are data instensive and performs simple operations, as a result, our PIM core doesn’t have any aggressive high performance/ILP techniques. It also has a SIMD unit as all of candidates we find benefit from parallelism.
For the PIM accelerator, for each of our PIM targets, we first design a customized in-memory logic unit, To benefit from parallelism, each PIM acceleartor has multiple copies of the in-memory logic unit,

## Slide 465: Workload Analysis
  Chrome
    Google’s web browser
TensorFlow
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video Codec
Notes: Now I’m gonna talk about our workload analysis. I will focus on chrome browser for the most of this talk.

## Slide 466: Workload Analysis
TensorFlow
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
  Chrome
    Google’s web browser

## Slide 467: How Chrome Renders a Web Page
HTML
CSS
HTML Parser
CSS Parser
Render Tree
Layout
Rasteriza-tion
Composit-ing
HTML
CSS
HTML Parser
CSS Parser
Loading and Parsing
Render Tree
Layout
Rasteriza-tion
Composi-ting
Painting

## Slide 468: How Chrome Renders a Web Page
HTML
CSS
HTML Parser
CSS Parser
Render Tree
Layout
Rasteriza-tion
Composi-ting
HTML
CSS
HTML Parser
CSS Parser
Loading and Parsing
Render Tree
Layout
Layouting
Rasteriza-tion
Composi-ting
Painting
paints those objects and generates the bitmaps
  calculates the visual elements and position of each object
assembles all layers into a final screen image
Notes: Feedback: the first major part just download the source files and parse them.
I just want to give you a brief high-level overview of how chrome renders a webpage. First the browser downloads the HTML and CSS, it starts parsing them to extract the content of the webpage. Then, based on those, at the next two stages, the browser calculate the visual rep and position of each object at the page. So at the end of layout stage, for each object, it knows the visual elements and the location of each object that needs to be drawn.. Then it goes to rasterization which is basically the process of painiting those object and generating the bitmaps. And at the final stages, compositing gets those bitmaps and composite them to gether and gerenate the final screen.
and calculate the visual represenation and postiion of each object in the page. At the end of the layout section,
Everything starts with downloading the HTML and CSS.
The chrome’s rendering engine, starts by parsing HTML files and store the the contents of a web page a tree of Node objects called the DOM tree. It also extracts style rules by parsing the CSS files. DOM tree and style rules together allows them to creates the render tree. The browser combines the DOM and style rules and generates "render tree,”. This tree is the visual representation of the document. The purpose of this tree is to enable painting the contents in their correct order. Up to this point we've calculated which nodes should be visible and their computed styles, but we have not calculated their exact position and size within the viewport of the device---that's the "layout" stage. Layout computes the exact position and size of each object.
Finally, now that we know which nodes are visible, and their computed styles and geometry, we can pass this information to the final stage, which converts each node in the render tree to actual pixels on the screen. This step is often referred to as "painting" or "rasterizing.” Painting is the process of filling in pixels into bitmaps. It involves drawing out text, colors, images, borders, and shadows, essentially every visual part of the elements. Finally, The rasterized bitmap (also known as a texture) is then sent to the GPU through a process called texture upload, after which the GPU performs compositing.
DOM: the contents of a web page are internally stored as a tree of Node objects called the DOM tree.
DOM: content of the webpage
Style rules: describe the style that need to be applies to the document
Render Tree: This tree is of visual elements in the order in which they will be displayed. It is the visual representation of the document. The purpose of this tree is to enable painting the contents in their correct order.
Layout: The calculation of geometric information (where and what size each element has) for every visible element. It’s normally done for the entire
Paint/rasterize: Painting is the process of filling in pixels. It involves drawing out text, colors, images, borders, and shadows, essentially every visual part of the elements. The drawing is typically done onto multiple surfaces, often called layers.
Compositing: Since the parts of the page were drawn into potentially multiple layers they need to be drawn to the screen in the correct order so that the page renders correctly. This is especially important for elements that overlap another, since a mistake could result in one element appearing over the top of another incorrectly.
https://aerotwist.com/blog/the-anatomy-of-a-frame/
The main subsystems are:
Input handling [technically not related to graphics per se, but nevertheless critical for many interactions]
Parsing, which turns a chunk of HTML into DOM nodes
Style, which resolves CSS onto the DOM
Layout, which figures out where DOM elements end up relative to one another
Paint setup, sometimes referred to as recording, which converts styled DOM elements into a display list (SkPicture) of drawing commands to paint later, on a per-layer basis
Painting, which converts the SkPicture of drawing commands into pixels in a bitmap somewhere (either in system memory or on the GPU if using Ganesh)
Compositing, which assembles all layers into a final screen image
and, less obviously, the presentation infrastructure responsible for actually pushing a new frame to the OS (i.e. the browser UI and its compositor, the GPU process which actually communicates with the GL driver, etc).

## Slide 469: Browser Analysis
To satisfy user experience, the browser must provide:
  Fast loading of webpages
  Smooth scrolling of webpages
  Quick switching between browser tabs
We focus on two important user interactions: 1) Page Scrolling 2) Tab Switching
  Both include page loading
Notes: So what are the important actions that users do with the browswe in the consumer devices?
The user perception of the browser speed is based on three factors: (1) page load time, (2) smooth web page scrolling, and (3) quick switching between browser tabs. In our study, we focus on two user interactions that impact these three factors, and govern a user’s browsing experience: (1) page scrolling and (2) tab switching. Note that each interaction includes page loading.
We emulate all these actions using Google’s temeletry freamework and focus on two actions:
Link it back to telemtery and probably remove the first bullet

## Slide 470
Scrolling
Notes: Now let me give you a little bit background on how prior works deal with the PIM coherence.

## Slide 471: What Does Happen During Scrolling?
HTML
CSS
HTML Parser
CSS Parser
Render Tree
Layout
Rasteriza-tion
Composi-itng
Layout
Rasteriza-tion
Composi-ting
    Rasterization generates the bitmap and sends it to GPU for compositing
Texture Tiling
to minimize cache misses during compositing, the graphics driver reorganizes the bitmaps
rasterization uses color blitters to convert the basic primitives into bitmaps
Color Blitting
Notes: When user scrolls a webpage, it triggers three operations in the browser. It forces the browser to recompute the layout because the position of each object has changed, it forces the browser to do rasterization, because there are some new contents that needs to be rasterized, and the browser need to do compositing because there are new objects that need to be displayed.
In addition to that, I want to briefly talk about two other important functions that play a key role in our analysis. The first one is Texture Tiling, that happens between rasterization and compositing. To minimze cache misses, the graphic drivers invokes texture tiling to reo-rganize the bitmaps before sending them to GPU. Another important function is color blitting. Color blitting is inoked during the rasterization. And it is used to convert the basic primitives like text and line, into bitmaps.

## Slide 472: Scrolling Energy Analysis
Chart: Fraction of Total Energy
| Google Docs | Gmail | Google Calendar | WordPress | Twitter | Animation | AVG
Texture Tiling | 1.312e+13 | 3.058e+12 | 319593492076.364 | 5.4789e+12 | 738397531219.6801 | 12302893814262 | 5.8363e+12
Color Blitting | 7.9639e+12 | 2.5555e+12 | 214665611070.8 | 1.9954e+12 | 539179828060.68 | 10082397746853 | 3.8919e+12
Other | 2.0596e+13 | 1.3368e+13 | 881303971032.8361 | 1.3228e+13 | 2.3356e+12 | 27432841968845 | 1.2973e+13
Google Docs
Gmail
Google Calendar
Word- Press
Twitter
Ani- mation
AVG
41.9% of page scrolling energy is spent on texture tiling and color blitting
Notes: Here I’m showing the energy breakdown for scrolling on different web pages. This figures shows what functions in browser consume the most of the energy when user do the scrolling. Across all of the pages that we test, 41.9% of page scrolling energy is spent on two data-intensive components: (1) texture tiling, where the graphics driver reorganizes the linear bitmap data into a tiled format for the GPU; and (2) color blitting, which is invoked by the Skia library [51] during rasterization.
The rest of the energy is spent on a variety of other libraries and functions, each of which contributes to less than 1% of the total energy consumption
So now the question is, where exactly the energy is spent in the system?

## Slide 473: Scrolling a Google Docs Web Page
A significant portion of total data movement comes from texture tiling and color blitting
77% of total energy consumption goes to data movement
37.7% of total system energy
Chart: Total Energy (pJ)
| CPU | L1 | LLC | Inter- connect | Mem Ctrl | DRAM
Texture Tiling | 2.5516e+12 | 903728069139.29 | 687788466859.2 | 2521647969456 | 403463675112.96 | 6.052e+12
Color Blitting | 3.0259e+12 | 531329645419 | 909145674584 | 982460247840 | 157193639654.4 | 2357904594816
Other | 4.2213e+12 | 2.5668e+12 | 2.3559e+12 | 3045626768304 | 487300282928.64 | 7.3095e+12
Chart: Fraction of Total Energy
| Texture Tiling | Color Blitting
Data Movement | 0.25733 | 0.12023
Compute | 0.062128 | 0.073675
Notes: To answer that question, here I’m showing the energy break down, across different hardware components in the consumer devices. The x axis shows how much energy is spent on each components like DRAM, caches or CPU, and the y axis shows the total energy.
A major observation from this figure is that majority of energy is spent on accessing data from DRAM, or on-chip caches, or moving data over interconnects. Our anlaysis shows that 77% of total energy goes to data movement. Our analysis show that almost half of that data movement comes from texture tiling and color blitting. Here I’m showsing that for each of those functions how much of the energy goes to data movement and computation. We find that these two functions are extermely data intensive and the data movement generate by these
To answer this question, we dig deeper into our energy analysis. This figure shows gives more insight into where energy is spent in the system when we scroll through a Google Docs. We find that 77% of the total energy consumption is due to data movement. The data movement energy includes the energy consumed by DRAM, the off-chip interconnect, and the on-chip caches.
We then zoom into each of those function and we find out that these functions are both very data intensive and majority of their energy goes to dat amovment. In fact we find that the data movement generated by texture tiling and color blitting alone accounts for 37.7% of the total system energy
OR
In fact, the data movement generated by these two functions account for 37.7 of total system energy.
When you present the question, you would say: we first need to see whats going on during texture tiling.
To answer this question, we need to first figure what each function does. We start by texture tiling.

## Slide 474: Scrolling a Google Docs Web Page
A significant portion of total data movement comes from texture tiling and color blitting
77% of total energy consumption goes to data movement
37.7% of total system energy
Chart: Total Energy (pJ)
| CPU | L1 | LLC | Inter- connect | Mem Ctrl | DRAM
Texture Tiling | 2.5516e+12 | 903728069139.29 | 687788466859.2 | 2521647969456 | 403463675112.96 | 6.052e+12
Color Blitting | 3.0259e+12 | 531329645419 | 909145674584 | 982460247840 | 157193639654.4 | 2357904594816
Other | 4.2213e+12 | 2.5668e+12 | 2.3559e+12 | 3045626768304 | 487300282928.64 | 7.3095e+12
Chart: Fraction of Total Energy
| Texture Tiling | Color Blitting
Data Movement | 0.25733 | 0.12023
Compute | 0.062128 | 0.073675
Can we use PIM to mitigate the data movement cost
for texture tiling and color blitting?
Notes: To answer that question, here I’m showing the energy break down, across different hardware components in the consumer devices. The x axis shows how much energy is spent on each components like DRAM, caches or CPU, and the y axis shows the total energy.
A major observation from this figure is that majority of energy is spent on accessing data from DRAM, or on-chip caches, or moving data over interconnects. Our anlaysis shows that 77% of total energy goes to data movement. Our analysis show that almost half of that data movement comes from texture tiling and color blitting. Here I’m showsing that for each of those functions how much of the energy goes to data movement and computation. We find that these two functions are extermely data intensive and the data movement generate by these
To answer this question, we dig deeper into our energy analysis. This figure shows gives more insight into where energy is spent in the system when we scroll through a Google Docs. We find that 77% of the total energy consumption is due to data movement. The data movement energy includes the energy consumed by DRAM, the off-chip interconnect, and the on-chip caches.
We then zoom into each of those function and we find out that these functions are both very data intensive and majority of their energy goes to dat amovment. In fact we find that the data movement generated by texture tiling and color blitting alone accounts for 37.7% of the total system energy
OR
In fact, the data movement generated by these two functions account for 37.7 of total system energy.
When you present the question, you would say: we first need to see whats going on during texture tiling.
To answer this question, we need to first figure what each function does. We start by texture tiling.

## Slide 475: Can We Use PIM for Texture Tiling?
time
CPU
Memory
Rasterization
Read Bitmap
Conversion
Write Back
data movement
CPU
PIM
CPU + PIM
Rasterization
Conversion
idle
1) Eliminate a significant portion of data movement
2) Free up CPU to perform
CPU-Only
Linear
Bitmap
Texture
Tiles
Invoke
Compositing
Invoke
Compositing
Linear
Bitmap
Texture
Tiles
Major sources of data movement: 1) poor data locality 2) large rasterized bitmap size (e.g. 4MB)
high
Texture Tiling
  Texture tiling is a good candidate for PIM execution
Notes: Feedback: move stuff from CPU-only to CPU+PIM, not fade
So can we use PIM for texture tiling? To answer that, here I’m showing you a bit more detailed of interactions between CPU and memory during texture tiling. As I said the cpu performs rasterization and store the bitmap in memory. It then needs to invoke Compositing process. Texture Tiling happens in between. The graphic driver read the bitmap, convert it to a more cache friendly format for GPU, and write it back to a location that GPU reads from.. It then invoke compositing. That’s where a lot of data movement happens because there is poor data locality during this processn and the bitmap sizes are so large that in some cases they don’t even fit into last level cache. This process is a good candidate for PIM. Here I’m showing what would happen if we move it to PIM. PIM logic access the bitmaps in memory, do the conversion, and write it to the location gpu access that. This way, it eliminates a significant porition of data movement and it also frees up the cpu to do other important task
So whats texture Tiglin. Here I want to walk you through the major steps during Texture tiling.
Texture tiling happens after rasterization and before compositing. Rasterization generates a rasterized bitmap. Then, that bitmap is sent to GPU for compositing. After rasterization, compositing accesses each texture in both the horizontal and vertical directions. To minimize cache misses during compositing, the graphics driver reads the rasterized bitmap ( 2 ) and converts the bitmap into a tiled texture layout
Because of this high amount of data movement, texture tiling is a good candidate for PIM execution. By moving texture tiling to PIM, we can let the PIM logic read the bitmap, performs the tiling operation in the memory, and the write it to a location that GPU will access. This wa,y we can elimnate a significant portion of data movement as it happens close to data and avoid moving the texture back and forth between memory and CPU . we can free up the CPU ( 5 ) to perform other important compute-intensive tasks in Chrome, such as handling user interaction, executing JavaScript code, or rasterizing other render objects.

## Slide 476: Can We Implement Texture Tiling in PIM Logic?
Requires simple primitives: memcopy, bitwise operations, and simple arithmetic operations
PIM Core
PIM Accelerator
Texture Tiling
Linear Bitmap
Tiled Texture
9.4% of the area available for PIM logic
7.1% of the area available for PIM logic
  PIM core and PIM accelerator are feasible to implement in-memory Texture Tiling
Notes: The next question is whether texture tiling is feasible to be implemented using PIM in consumer devices. To answer that, we analyze the texutre tiling in detail and find that
hat texture tiling requires only simple primitives: memcopy, bitwise operations, and simple arithmetic operations (e.g., addition).
These operations can be performed at high performance on our PIM core, and they can easily be implemented as a fixed function PIM accelerator.
Our analysis hsows that each of them takes less than 10% of the area available per vault, and as a result, both are feasible to implement in a consumer device with 3D-stacked memory
As we explained before our PIM core is …
Our PIM accelerator for texture tiling consists of multiple in-memory tiling units.
Each in-memory tiling unit consists of only a simple ALU, and operates on a single 4 kB tile.
We empirically decide to use four in-memory tiling units in each PIM accelerator
We conclude that the area required for texture tiling PIM logic is small, making the PIM logic feasible to implement in a consumer device with 3D-stacked memory

## Slide 477: Color Blitting Analysis
Color blitting is a good candidate
for PIM execution
It is feasible to implement color blitting in PIM core and PIM accelerator
Generates a large amount of data movement
Requires low-cost operations: Memset, simple arithmetic, and shift operations
  Accounts for 19.1% of the total system energy during scrolling
Notes: We did the same analysis for Color Blitting. Because of lack of time, I will talk about the key points here.
Majority come from its streaming access pattern and the large sizes of the bitmaps (e.g., 1024x1024 pixels).
The function itself require simple computations

## Slide 478: Scrolling Wrap Up
Texture tiling and color blitting account for a significant portion (41.9%) of energy consumption
37.7% of total system energy goes to data movement generated by these functions
  Both functions can benefit significantly from PIM execution
  Both functions are feasible to implement as PIM logic
1
2
Notes: So here I just want to wrap up our analysis for page scrolling. We found two data intensive functions that account for a significant portion of energy during scrolling. We find that both function can significantly benfti from PIM execution. We also find that both functions are simple enough that can be impelemented at pim logic

## Slide 479
Tab Switching
Notes: Now let me give you a little bit background on how prior works deal with the PIM coherence.

## Slide 480: What Happens During Tab Switching?
Chrome employs a multi-process architecture
  Each tab is a separate process
Main operations during tab switching:
  Context switch
  Load the new page
Chrome Process
…
Tab 1 Process
Tab 2 Process
Tab N Process
Notes: Chrome uses a multi-process architecture, where each tab has its own application process for rendering the page displayed in the tab to improve reliability and performance.
When a user switches between browser tabs, this triggers two operations: (1) a context switch to the process for the selected tab, and (2) a load operation for the new page.

## Slide 481: Memory Consumption
Primary concerns during tab switching:
  How fast a new tab loads and becomes interactive
  Memory consumption
CPU
DRAM
Inactive Tab
Compression
Decompression
Chrome uses compression to reduce each tab’s memory footprint
ZRAM
Compressed Tab
Notes: There are two primary concerns during tab switching: (1) how fast a new tab loads and becomes interactive, as this directly affects user satisfaction; and (2) memory consumption.
Memory consumption is a major concern for three reasons. First, the average memory footprint of a web page has increased significantly in recent years because of increased use of images, JavaScript, and video in modern web pages. Second users tend to open multiple tabs at a time with each tab consuming additional memory. Third, consumer devices typically have a much lower memory capacity than server or desktop systems, and without careful memory management, Chrome could run out of memory on these systems over time.

## Slide 482: Data Movement Study
To study data movement during tab switching, we emulate a user switching through 50 tabs
Compression and decompression contribute to18.1% of the total system energy
19.6 GB of data moves between CPU and ZRAM
2
1
We make two key observations:
Notes: Moves between CPU and ZRAM
There are two primary concerns during tab switching: (1) how fast a new tab loads and becomes interactive, as this directly affects user satisfaction; and (2) memory consumption.
Memory consumption is a major concern for three reasons. First, the average memory footprint of a web page has increased significantly in recent years because of increased use of images, JavaScript, and video in modern web pages. Second users tend to open multiple tabs at a time with each tab consuming additional memory. Third, consumer devices typically have a much lower memory capacity than server or desktop systems, and without careful memory management, Chrome could run out of memory on these systems over time.

## Slide 483: Can We Use PIM to Mitigate the Cost?
CPU
CPU-Only
Memory
CPU
CPU + PIM
PIM
time
Swap out N pages
Read N Pages
Compress
Other tasks
Write back
compression
ZRAM
Swap out N pages
Other tasks
Compress
ZRAM
No off-chip data movement
  PIM core and PIM accelerator are feasible to implement in-memory compression/decompression
data movement
high
Uncompressed
Pages
Uncompressed
Pages
Notes: Now we want to see if we can mitigate data movement cost with PIM. To answer that, lets again take a look at interaction between CPU and memory when CPU wants to swap out N pages. we need to figure out where the data movement happens. Here shows what happens when CPU wants to swap out N inactive pages. it first read the inactive page data, compress the data ( 2 ), and write the compressed data to ZRAM. This incur a lot of overhead. This operation is a good fit for PIM as (1) it cause a large amount of data movement; and (2) compression can be handled in the background, since none of the active tab processes need the data that is being compressed
Our analysis shows that the compression algorithm used by chrome is simple enough that both pim core and …
To wrap up, we found that a lot of data movement happens during tab switching as chrome tries to compress and decompress tabs. We find that both compression and decompression can significantly benefit from PIM execution and are feasible to be implemented at PIM logic
Now on the right what happens when we offload compression to PIM. In this case, the CPU only informs the PIM logic about the pages that need to be swapped out, and the PIM logic operates on the uncompressed page data that is already in memory. This (1) eliminates the off-chip page data movement that took place during CPU-based compression, and (2) frees up the CPU to perform other tasks while PIM performs compression in the background. We observe a similar behavior during decompression.

## Slide 484: Tab Switching Wrap Up
A large amount of data movement happens during tab switching as Chrome attempts to compress and decompress tabs
2
  Both functions can benefit from PIM execution and can be implemented as PIM logic
Notes: To wrap up, we found that a lot of data movement happens during tab switching as chrome tries to compress and decompress tabs. We find that both compression and decompression can significantly benefit from PIM execution and are feasible to be implemented at PIM logic

## Slide 485: Workload Analysis
  Chrome
    Google’s web browser
TensorFlow
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec

## Slide 486: Workload Analysis
  Chrome
    Google’s web browser
TensorFlow
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec

## Slide 487: TensorFlow Mobile
57.3% of the inference energy is spent on data movement
54.4% of the data movement energy comes from packing/unpacking and quantization
Inference
Prediction

## Slide 488: Packing
Reorders elements of matrices to minimize cache misses during matrix multiplication
Up to 40% of the inference energy and 31% of inference execution time
Packing’s data movement accounts for up to 35.3% of the inference energy
Packing
Matrix
Packed Matrix
A simple data reorganization process that requires simple arithmetic

## Slide 489: Quantization
Converts 32-bit floating point to 8-bit integers to improve inference execution time and energy consumption
Up to 16.8% of the inference energy and 16.1% of inference execution time
Majority of quantization energy comes from data movement
Quantization
floating point
integer
A simple data conversion operation that requires shift, addition, and multiplication operations

## Slide 490: Quantization
Converts 32-bit floating point to 8-bit integers to improve inference execution time and energy consumption
Up to 16.8% of the inference energy and 16.1% of inference execution time
Majority of quantization energy comes from data movement
Quantization
floating point
integer
A simple data conversion operation that requires shift, addition, and multiplication operations
Based on our analysis, we conclude that:
Both functions are good candidates for PIM execution
It is feasible to implement them in PIM logic

## Slide 491: Video Playback and Capture
Compressed video
VP9 Decoder
Display
Captured video
VP9 Encoder
Compressed video
Majority of energy is spent on data movement
Majority of data movement comes from simple functions in decoding and encoding pipelines
Notes: We also analyze video play back and video capture. We take a look at energy consumption when vp9 decider is yaed to playback a netflix film, and when vp9 wncoder is used to do real-time encoding of ...
We find that for both of these workloads data movemwnt is a major contributor to the total system enery.
When we dog deeper we find that they are simple functions in decoding and encoding pipeline that generate the majority of dara movement.
Please refer to the paper for more detail.

## Slide 492: Outline
  Introduction
  Background
  Analysis Methodology
  Workload Analysis
  Evaluation
  Conclusion

## Slide 493: Evaluation Methodology
System Configuration (gem5 Simulator)
  SoC: 4 OoO cores, 8-wide issue, 64 kB L1cache, 2MB L2 cache
  PIM Core: 1 core per vault, 1-wide issue, 4-wide SIMD, 32kB L1 cache
  3D-Stacked Memory: 2GB cube, 16 vaults per cube
    Internal Bandwidth: 256GB/S
    Off-Chip Channel Bandwidth: 32 GB/s
  Baseline Memory: LPDDR3, 2GB, FR-FCFS scheduler
We study each target in isolation and emulate each separately and run them in our simulator
Notes: and then analyzing the benefit of PIM in our simulator

## Slide 494: Normalized Energy
Chart: Normalized Energy
| Texture Tiling | Color Blitting | Com- pression | Decom- pression | Packing | Quantization | Sub-Pixel Interpolation | Deblocking Filter | Motion Estimation
CPU-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Core | 0.41638 | 0.531 | 0.59396 | 0.40527 | 0.5087 | 0.50462 | 0.50061 | 0.49893 | 0.59594
PIM-Acc | 0.36127 | 0.42335 | 0.47294 | 0.29851 | 0.47245 | 0.42913 | 0.34481 | 0.26459 | 0.3925
Chrome Browser
Video Playback and Capture
TensorFlow Mobile
PIM core and PIM accelerator reduces energy consumption on average by 49.1% and 55.4%
77.7% and 82.6% of energy reduction for texture tiling and packing comes from eliminating data movement
Notes: We make another obsrevation that using PIM accelerator provide limited energy reduction over PIM core, for some of these workloads, such as texture tiling. This is becase these kernels are data intensive and have low ocmputational compleity, and as a result, using fixed function accelerator does not provide significant energy reduction over the PIM core.

## Slide 495: Normalized Runtime
Chart: Normalized Runtime
| Texture Tiling | Color Blitting | Comp- ression | Decomp- ression | Sub-Pixel Interpolation | Deblocking Filter | Motion Estimation | TensorFlow
CPU-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Core | 0.43478 | 0.64516 | 0.76336 | 0.76923 | 0.72464 | 0.8 | 0.84746 | 0.63694
PIM-Acc | 0.4 | 0.57803 | 0.47619 | 0.5 | 0.5814 | 0.70423 | 0.47619 | 0.50505
Chrome Browser
Video Playback and Capture
TensorFlow Mobile
Offloading these kernels to PIM core and PIM accelerator improves performance on average by 44.6% and 54.2%
Notes: PIM-Core and PIM-Acc significantly outperform CPU-Only across all kernels, improving performance by … This perfomance benefit come from higher bandwidth and lower access latency of 3D-stacked memory, because all of these kernels are data intensive.
Performance improvement of PIM-acc over PIM-core differes across different workloads. In some cases such as Texture Tiling, the performance improvement of PIM-Acc over PIM-Core is limited by the low computational complexity of these two kernels. But there are other cases, such as compression that benefit significantly from using PIM-Acc over PIM-Core in terms of performance, because these kernels are more compute-intensive and less data-intensive compared to texture tiling and.

## Slide 496: Conclusion
Energy consumption is a major challenge in consumer devices
We conduct an in-depth analysis of popular Google consumer workloads
  62.7% of the total system energy is spent on data movement
  Most of the data movement comes from simple functions that consist of simple operations
We use PIM to reduce data movement cost
  We design lightweight logic to implement simple operations in DRAM
  Reduces total energy by 55.4% on average
  Reduces execution time by 54.2% on average
PIM Core
PIM Accelerator
PIM Accelerator
PIM Accelerator

## Slide 497: Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Amirali Boroumand
Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun,
Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu

## Slide 498: End of Backup Slides