## Slide 1: Memory-Centric Computing
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
9 February 2022
Intel Interconnect & Connectivity Summit Keynote Speech

## Slide 2: The Problem
Computing
is Bottlenecked by Data

## Slide 3: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate more than we can process

## Slide 4: Data is Key for Future Workloads
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 5: Data Overwhelms Modern Machines
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Data → performance & energy bottleneck

## Slide 6
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data is Key for Future Workloads
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 7
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 8: Data is Key for Future Workloads
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 9
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Data → performance & energy bottleneck
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 10: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version]
Oxford Nanopore MinION

## Slide 11: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION
Data → performance & energy bottleneck

## Slide 12: Accelerating Genome Analysis [IEEE MICRO 2020]
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 13: FPGA-based Near-Memory Analytics
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), 2021.

## Slide 14: GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 15: In-Storage Genome Filtering [ASPLOS 2022]

## Slide 16: Future of Genome Sequencing & Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 17: More on Fast & Efficient Genome Analysis …
Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" Invited Lecture at Technion, Virtual, 26 January 2021. [Slides (pptx) (pdf)] [Talk Video (1 hour 37 minutes, including Q&A)] [Related Invited Paper (at IEEE Micro, 2020)]
https://www.youtube.com/watch?v=r7sn41lH-4A

## Slide 18: Detailed Lectures on Genome Analysis
Computer Architecture, Fall 2020, Lecture 3a
  Introduction to Genome Sequence Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=CrRb32v7SJc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=5
Computer Architecture, Fall 2020, Lecture 8
  Intelligent Genome Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=ygmQpdDTL7o&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=14
Computer Architecture, Fall 2020, Lecture 9a
  GenASM: Approx. String Matching Accelerator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=XoLpzmN-Pas&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=15
Accelerating Genomics Project Course, Fall 2020, Lecture 1
  Accelerating Genomics (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=rgjl8ZyLsAg&list=PL5Q2soXY2Zi9E2bBVAgCqLgwiDRQDTyId
https://www.youtube.com/onurmutlulectures

## Slide 19: Data Overwhelms Modern Machines …
Storage/memory capability
Communication capability
Computation capability
Greatly impacts robustness, energy, performance, cost

## Slide 20: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 21: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data
Yet, system is still bottlenecked by memory

## Slide 22
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 23
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement
Data Movement Overwhelms Modern Machines

## Slide 24: Axiom
An Intelligent Architecture
Handles Data Well

## Slide 25: How to Handle Data Well
Ensure data does not overwhelm the components
  via intelligent algorithms
  via intelligent architectures
  via whole system designs: algorithm-architecture-devices
Take advantage of vast amounts of data and metadata
  to improve architectural & system-level decisions
Understand and exploit properties of (different) data
  to improve algorithms & architectures in various metrics

## Slide 26: Corollaries: Architectures Today …
Architectures are terrible at dealing with data
  Designed to mainly store and move data vs. to compute
  They are processor-centric as opposed to data-centric
Architectures are terrible at taking advantage of vast amounts of data (and metadata) available to them
  Designed to make simple decisions, ignoring lots of data
  They make human-driven decisions vs. data-driven
Architectures are terrible at knowing and exploiting different properties of application data
  Designed to treat all data as the same
  They make component-aware decisions vs. data-aware

## Slide 27: Fundamentally Better Architectures
Data-centric
Data-driven
Data-aware

## Slide 28: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 29: Axiom
To achieve the highest energy efficiency and performance:
we must take an expanded view
of computer architecture
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Co-design across the hierarchy:
Algorithms to devices
Specialize as much as possible
within the design goals

## Slide 30: Fundamentally Better Architectures
Data-centric
Data-driven
Data-aware

## Slide 31: Data-Centric (Memory-Centric) Architectures

## Slide 32: Data-Centric Architectures: Properties
Process data where it resides (where it makes sense)
  Processing in and near memory structures
Low-latency and low-energy data access
  Low latency memory
  Low energy memory
Low-cost data storage and processing
  High capacity memory at low cost: hybrid memory, compression
Intelligent data management
  Intelligent controllers handling robustness, security, cost, perf.

## Slide 33: Processing Data Where It Makes Sense

## Slide 34: Processing in/near Memory: An Old Idea
Kautz, “Cellular Logic-in-Memory Arrays”, IEEE TC 1969.
https://doi.org/10.1109/T-C.1969.222754

## Slide 35: Processing in/near Memory: An Old Idea
Stone, “A Logic-in-Memory Computer,” IEEE TC 1970.
https://safari.ethz.ch/architecture/fall2020/lib/exe/fetch.php?media=stone_logic_in_memory_1970.pdf

## Slide 36: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures

## Slide 37: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
[UPMEM 2019]
[Samsung 2021]

## Slide 38: Memory Scaling Issues Were Real
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Proceedings of the 5th International Memory Workshop (IMW), Monterey, CA, May 2013. Slides (pptx) (pdf) EETimes Reprint
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 39: As Memory Scales, It Becomes Unreliable
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 40
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 41: The Story of RowHammer Lecture …
Onur Mutlu, "The Story of RowHammer" Keynote Talk at Secure Hardware, Architectures, and Operating Systems Workshop (SeHAS), held with HiPEAC 2021 Conference, Virtual, 19 January 2021. [Slides (pptx) (pdf)] [Talk Video (1 hr 15 minutes, with Q&A)]
https://www.youtube.com/watch?v=sgd7PHQQ1AI

## Slide 42: Memory Scaling Issues Are Real
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 43: Memory Scaling Issues Are Real
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version] [Slides from COSADE 2019 (pptx)] [Slides from VLSI-SOC 2020 (pptx) (pdf)] [Talk Video (1 hr 15 minutes, with Q&A)]

## Slide 44: Hybrid Memory Enables Better Scaling
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation & movement
to achieve the best of multiple technologies

## Slide 45: The Push from Circuits and Devices
Main Memory Needs
Intelligent Controllers

## Slide 46: An Example Intelligent Controller
A. Giray Yaglikci, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (22 minutes)] [Short Talk Video (7 minutes)]

## Slide 47: Industry Is Writing Papers About It, Too

## Slide 48: Call for Intelligent Memory Controllers

## Slide 49: Another Example Intelligent Controller
Minesh Patel, Geraldo F. de Oliveira Jr., and Onur Mutlu, "HARP: Practically and Effectively Identifying Uncorrectable Errors in Memory Chips That Use On-Die Error-Correcting Codes" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (1.5 minutes)] [HARP Source Code (Officially Artifact Evaluated with All Badges)]

## Slide 50: The Takeaway
Intelligent
Memory Controllers
Can Avoid Many Failures
& Enable Better Scaling

## Slide 51: The Push from Circuits and Devices
Main Memory Needs
Intelligent Controllers

## Slide 52: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
Pull from Systems and Applications
  Data access is a major system and application bottleneck
  Systems are energy limited
  Data movement much more energy-hungry than computation

## Slide 53: Three Key Systems & Application Trends
1. Data access is a major bottleneck
  Applications are increasingly data hungry
2. Energy consumption is a key limiter
3. Data movement energy dominates compute
  Especially true for off-chip to on-chip movement

## Slide 54: Do We Want This?
Source: V. Milutinovic

## Slide 55: Or This?
Source: V. Milutinovic

## Slide 56: Challenge and Opportunity for Future
High Performance,
Energy Efficient,
Sustainable

## Slide 57: The Problem
Data access is the major performance and energy bottleneck
Our current
design principles
cause great energy waste
(and great performance loss)

## Slide 58: The Problem
Processing of data
is performed
far away from the data

## Slide 59: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 60: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 61: Today’s Computing Systems
Are overwhelmingly processor centric
All data processed in the processor  at great system cost
Processor is heavily optimized and is considered the master
Data storage units are dumb and are largely unoptimized

## Slide 62: Yet …
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 63: The Performance Perspective
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors" Proceedings of the 9th International Symposium on High-Performance Computer Architecture (HPCA), pages 129-140, Anaheim, CA, February 2003. Slides (pdf)
  One of the 15 computer arch. papers of 2003 selected as Top Picks by IEEE Micro. HPCA Test of Time Award (awarded in 2021).

## Slide 64: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 65: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 66: Perils of Processor-Centric Design
Grossly-imbalanced systems
  Processing done only in one place
  All else just stores and moves data: data moves a lot
   Energy inefficient
   Low performance
   Complex
Overly complex and bloated processor (and accelerators)
  To tolerate data access from memory
  Complex hierarchies and mechanisms
   Energy inefficient
   Low performance
   Complex

## Slide 67: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data
Yet, system is still bottlenecked by memory

## Slide 68: The Energy Perspective
Dally, HiPEAC 2015

## Slide 69: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 70: Data Movement vs. Computation Energy
Data movement is a major system energy bottleneck
  Comprises 41% of mobile system energy during web browsing [2]
  Costs ~115 times as much energy as an ADD operation [1, 2]
[1]: Reducing data Movement Energy via Online Data Clustering and Encoding (MICRO’16)
[2]: Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms (IISWC’14)

## Slide 71: Energy Waste in Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 72: We Do Not Want to Move Data!
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 73: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 74: Goal: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processors & communication units?
  software & hardware interfaces?
  system software, compilers, languages?
  algorithms & theoretical foundations?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 75: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 78: We Need to Think Differently from the Past Approaches

## Slide 79: Processing in Memory: Two Approaches
1. Processing using Memory
2. Processing near Memory

## Slide 80: Two PIM Approaches
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021. [Tutorial Video on "Memory-Centric Computing Systems" (1 hour 51 minutes)]
https://people.inf.ethz.ch/omutlu/pub/ModernPrimerOnPIM_springer-emerging-computing-bookchapter21.pdf

## Slide 81: Approach 1: Processing Using Memory
Take advantage of operational principles of memory to perform bulk data movement and computation in memory
  Can exploit internal connectivity to move data
  Can exploit analog computation capability
  …
Examples: RowClone, In-DRAM AND/OR, Gather/Scatter DRAM
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)
  "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology” (Seshadri et al., MICRO 2017)

## Slide 82: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 83: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 84: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 85: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 86: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 87: Real System RowClone Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram

## Slide 88: Lecture on RowClone & Processing using DRAM
https://www.youtube.com/watch?v=n6Pwg1qax_E&list=PL5Q2soXY2Zi_7UBNmC9B8Yr5JSwTG9yH4&index=4

## Slide 89: Mindset: Memory as an Accelerator
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 90: (Truly) In-Memory Computation
We can support in-DRAM AND, OR, NOT, MAJ
At low cost
Using analog computation capability of DRAM
  Idea: activating multiple rows performs computation
30-60X performance and energy improvement
  Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
New memory technologies enable even more opportunities
  Memristors, resistive RAM, phase change mem, STT-MRAM, …
  Can operate on data with minimal movement

## Slide 91: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 92: Bulk Bitwise Operations in Workloads
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017

## Slide 93: In-DRAM Acceleration of Database Queries
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 94: More on Ambit
Vivek Seshadri, Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 95: In-DRAM Bulk Bitwise Execution
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]

## Slide 96: SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 97: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program

## Slide 98: SIMDRAM Key Results
Evaluated on:
  16 complex in-DRAM operations
  7 commonly-used real-world applications
SIMDRAM provides:
88× and 5.8× the throughput of a CPU and a high-end GPU, respectively, over 16 operations
257× and 31× the energy efficiency of a CPU and a high-end GPU, respectively, over 16 operations
21× and 2.1× the performance of a CPU an a high-end GPU, over seven real-world applications

## Slide 99: More on SIMDRAM
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 100: In-DRAM Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 101: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 102: In-DRAM True Random Number Generation
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 103: Processing in Memory: Two Approaches
1. Processing using Memory
2. Processing near Memory

## Slide 104: Specialization: In-Memory Graph Processing
Large graphs are everywhere (circa 2015)
Scalable large-scale graph processing is challenging
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos
Chart: Speedup
| 128 Cores | 32 Cores
열3 | 1.4206 | 1

## Slide 105: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 106: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 107: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 108: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communications via Remote Function Calls

## Slide 109: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 110: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
Tesseract
32 Tesseract Cores
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 111: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
On five graph processing algorithms

## Slide 112: Tesseract Graph Processing System Energy
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
> 8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 113: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 114: Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks
Amirali Boroumand
Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun,
Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, Onur Mutlu

## Slide 115: Consumer Devices
Consumer devices are everywhere!
Energy consumption is a first-class concern in consumer devices
Notes: Consumer devices like tablets smartphone and wearable are now everywhere and used by billions of people.
One of the major challenge in these devices is battery limitation which makes the energy consumption a critical concern …

## Slide 116: Popular Consumer Workloads
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 117: Energy Cost of Data Movement
Data Movement
1st key observation: 62.7% of the total system energy is spent on data movement
  Potential solution: move computation close to data
  Challenge: limited area and energy budget
Processing-In-Memory (PIM)
SoC
DRAM
L2
L1
CPU
CPU
CPU
CPU
Compute Unit
Notes: Throughout our analysis, we make a key observation that out of all sources of energy consumption, data movement is a major contributor to the total system energy. We find that across all of the workloads, on average around 62.7% of total system energy is spent on data movement.
One way to reduce data movement cost is to move computation close to data, or …
One potential solution to address this cost it do move computation close to data, or in other words, do procesing in memory. However, the challenge is that these devices.
One potential solution to mitigate data movement cost and reduce total system energy is to execute data-movement heavy portions of application close to data, or in other words, do processing in memory. However, consumer devices are extermely limited in terms of area and power budget. So the question is can we move part of the data movement heavy portion given the limited area and energy budget. Our

## Slide 118: Using PIM to Reduce Data Movement
  2nd key observation: a significant fraction of the data movement often comes from simple functions
PIM Core
PIM Accelerator
PIM Accelerator
PIM Accelerator
We can design lightweight logic to implement these simple functions in memory
Small embedded low-power core
Small fixed-function accelerators
  Offloading to PIM logic reduces energy and improves performance, on average, by 2.3X and 2.2X
Notes: To figure out if we can use processing in memory, we dig deeper into our analysis and we make another key observation that majority of data movement often comes form simple functions and pritmitives. We find that these simple function can be implemented in memory as either a small embedded core, or group of small fixed function accelerators. Our result shows that offloading these function to PIM logic can significantly reduce data movement for each function and reduce energy on average around 55% and improve perforamcne around 54%.
our PIM core can reduce significant portion of data movement, reduce enregy by 49.1% for each function and improve performance up to 2.2X. While using group of fixed function accelerator reduce energy by 55.4% and improve performance by up to 2.5X.
  Or use Saugata’s approach : Reduces total system energy by an average of 55.4%
  Reduces execution time by an average of 54.2%
Our result show that both of them can significantly reduce the data movement for each function.
Feedback: talk about result more
Don’t talk about specific detail like MemCopy, MemSet stuff like that
Main take away: data movement come from simple functions that are simple enough to implement in PIM
We find that these functions and primitves can be implemented as PIM logic using either (1) a small low-power general-purpose embedded core or (2) a group of small fixed-function accelerators (PIM accelerators). Our Analysis shows that both are cost-feasible to use in consumer devices. We find that they eliminate a significant fraction of dat amovement, and reduce energy consumption for each of these operation on average by 49 and 55%.

## Slide 119: Workload Analysis
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 120: TensorFlow Mobile
57.3% of the inference energy is spent on data movement
54.4% of the data movement energy comes from packing/unpacking and quantization
Inference
Prediction

## Slide 121: More on PIM for Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Lightning Talk Video (2 minutes)] [Full Talk Video (21 minutes)]

## Slide 122: Truly Distributed GPU Processing with PIM
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
SM (Streaming Multiprocessor)

## Slide 123: Accelerating GPU Execution with PIM (I)
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 124: Accelerating GPU Execution with PIM (II)
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 125: Accelerating Linked Data Structures
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 126: Accelerating Dependent Cache Misses
Milad Hashemi, Khubaib, Eiman Ebrahimi, Onur Mutlu, and Yale N. Patt, "Accelerating Dependent Cache Misses with an Enhanced Memory Controller" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 127: Accelerating Runahead Execution
Milad Hashemi, Onur Mutlu, and Yale N. Patt, "Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads" Proceedings of the 49th International Symposium on Microarchitecture (MICRO), Taipei, Taiwan, October 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pdf)] [Poster (pptx) (pdf)]

## Slide 128: Accelerating Climate Modeling
Gagandeep Singh, Dionysios Diamantopoulos, Christoph Hagleitner, Juan Gómez-Luna, Sander Stuijk, Onur Mutlu, and Henk Corporaal, "NERO: A Near High-Bandwidth Memory Stencil Accelerator for Weather Prediction Modeling" Proceedings of the 30th International Conference on Field-Programmable Logic and Applications (FPL), Gothenburg, Sweden, September 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (23 minutes)] Nominated for the Stamatis Vassiliadis Memorial Award.

## Slide 129: Accelerating Approximate String Matching
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 130: Accelerating Time Series Analysis
Ivan Fernandez, Ricardo Quislant, Christina Giannoula, Mohammed Alser, Juan Gómez-Luna, Eladio Gutiérrez, Oscar Plata, and Onur Mutlu, "NATSA: A Near-Data Processing Accelerator for Time Series Analysis" Proceedings of the 38th IEEE International Conference on Computer Design (ICCD), Virtual, October 2020. [Slides (pptx) (pdf)] [Talk Video (10 minutes)] [Source Code]

## Slide 131: Accelerating Neural Network Inference
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]

## Slide 132: Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks
Amirali Boroumand Saugata Ghose Berkin Akin
Ravi Narayanaswami Geraldo F. Oliveira Xiaoyu Ma
Eric Shiu Onur Mutlu
PACT 2021
Notes: Hi, I’m Geraldo, a PhD Student at ETH Zurich.
Today I will present our work “Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks”
This work was lead by Amirali Boroumand during his internship at Google.

## Slide 133: Executive Summary
Context: We extensively analyze a state-of-the-art edge ML accelerator (Google Edge TPU) using 24 Google edge models
  Wide range of models (CNNs, LSTMs, Transducers, RCNNs)
Problem: The Edge TPU accelerator suffers from three challenges:
  It operates significantly below its peak throughput
  It operates significantly below its theoretical energy efficiency
  It inefficiently handles memory accesses
  Key Insight: These shortcomings arise from the monolithic design of the Edge TPU accelerator
  The Edge TPU accelerator design does not account for layer heterogeneity
  Key Mechanism: A new framework called Mensa
  Mensa consists of heterogeneous accelerators whose dataflow and hardware are specialized for specific families of layers
  Key Results: We design a version of Mensa for Google edge ML models
  Mensa improves performance and energy by 3.0X and 3.1X
  Mensa reduces cost and improves area efficiency
Notes: First, I will give an overview of this work.
[CLICK] In this work, we extensively analyze 24 edge NN models from Google while running inference on the Google Edge TPU accelerator for various types of NN models
[CLICK] We identify that while running NN inference, the accelerator suffers from three main challenges
[CLICK] it operates significantly below its peak throughput
[CLICK] it operates significantly below its theorical peak energy efficiency
[CLICK] and its memory system is not efficient
[CLICK] Our analysis leads to the key insight that these challenges arrive due to the monolithic one-size-fit-all design of the accelerators, which does not account for heterogeneity across different NN layers
[CLICK] To solve this issue, we propose Mensa, a framework that maps the execution of a particular NN layer to its most appropriate hardware accelerator
[CLICK] We extensively evaluate Mensa for Google NN models and we observe that it improves performance and energy efficiency by 3.0x and 3.1x compared to the baseline Edge TPU accelerator while reducing area and cost across 24 edge ML models
[NEXT]

## Slide 134: Google Edge Neural Network Models
  We analyze inference execution using 24 edge NN models
13 CNN
Face Detection
6 RNN Transducers
Speech Recognition
2 LSTMs
Language Translation
Image Captioning
3 RCNN
Google Edge TPU
Notes: [CLICK] We analyze inference execution on the accelerator using 24 edge NN models that serve as internal benchmarks for the Google Edge TPU, including
[CLICK] 6 RNN Transducers, used for applications such as automatic speech recognition.
[CLICK] 13 convolutional neural networks (CNNs), typically used for applications such as image classification and object detection
[CLICK] 2 long short-term memories (LSTMs), used for applications such as language translation and and handwriting recognition, and
[CLICK] 3 recurrent convolutional neural networks (RCNNs), used for applications such as image captioning
[NEXT]

## Slide 135: Diversity Across the Models
Insight 1: there is significant variation in terms of layer characteristics across the models
Chart: Parameter Footprint (MB)
| 1.0986329999999999E-3
CNN3 | 22201
CNN3 | 21609
CNN3 | 11025
CNN3 | 1225
CNN4 | 5329
CNN4 | 5041
CNN4 | 5329
CNN4 | 2628
CNN11 | 3136
CNN11 | 12544
CNN3 | 1
CNN4 | 1
Layers from LSTMs and Transducers
Layers from CNNs and RCNNs
Notes: We draw key two insights from our model analysis
[CLICK] First, we observe a large variation in terms of layer characteristics across different models.
[CLICK] To illustrate, the figure shows the total parameter footprint vs. the FLOP/B ratio (or reuse) across the layers of representative CNNs, LSTMs, and Transducers
[CLICK] We observe from the figure that that layers from LSTMs and Transducers have larger parameter footprints and lower reuse than layers from CNNs.
[NEXT]

## Slide 136: Diversity Within the Models
For example, our analysis of edge CNN models shows:
1
2
Insight 2: even within each model, layers exhibit
significant variation in terms of layer characteristics
Chart: CNN5
 | 150.0625 | 12.25 | 110.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 27.5625 | 12.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 27.5625 | 12.25 | 98 | 24.5 | 110.25 | 49 | 49 | 110.25 | 49 | 49 | 110.25 | 49 | 95.7031 | 25.375 | 24.5 | 25.375 | 24.5 | 25.375 | 24.5 | 25.375 | 24.5 | 13.7812 | 13.7812 | 24.5 | 24.5 | 12.25 | 110.25
Chart: CNN13
Variation in FLOP/Byte: up to 244x across layers
Variation in MAC intensity: up to 200x across layers
Notes: [CLICK] Second, even within a single model, layers show variation in terms of layer characteristics
[CLICK] For example, we observe that layers in a single CNN models show
[CLICK] a varying MAC intensity of up to 200x across different layers
and
[CLICK] a varying flop/byte ratio of up to 244x across different layers
[NEXT]

## Slide 137: Mensa High-Level Overview
Monolithic Accelerator
Model A
Family 2
Family 3
Edge TPU Accelerator
Mensa
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Model B
Model C
Model A
Model B
Model C
Runtime
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Family 1
Acc. 1
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Acc. 2
Buffer
NoC
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
Acc. 3
Notes: [CLICK ] In a baseline system, different machine learning models are execute in a single, monolithic edge accelerator, which leads to performance and energy issues.
[CLICK] On the other hand, Mensa distributes the layers from an NN model using a runtime scheduler across a collection of smaller hardware accelerators that are catered the properties of different layer types. By specializing each accelerator to a subset of layers, Mensa avoids the shortcomings of current monolithic edge ML accelerators, resulting in a highly-efficient and high-performance accelerator with a much smaller area.
Next I will give an brief overview of Mensa’s ruy
[NEXT]

## Slide 138: Mensa: Highly-Efficient ML Inference
Amirali Boroumand, Saugata Ghose, Berkin Akin, Ravi Narayanaswami, Geraldo F. Oliveira, Xiaoyu Ma, Eric Shiu, and Onur Mutlu, "Google Neural Network Models for Edge Devices: Analyzing and Mitigating Machine Learning Inference Bottlenecks" Proceedings of the 30th International Conference on Parallel Architectures and Compilation Techniques (PACT), Virtual, September 2021. [Slides (pptx) (pdf)] [Talk Video (14 minutes)]

## Slide 139: FPGA-based Processing Near Memory
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), 2021.

## Slide 140: Near-Memory Acceleration using FPGAs
IBM POWER9 CPU
HBM-based FPGA board
OCAPI
Source: AlphaData
Source: IBM
Near-HBM FPGA-based accelerator
Two communication technologies: CAPI2 and OCAPI
Two memory technologies: DDR4 and HBM
Two workloads: Weather Modeling and Genome Analysis
Notes: To this end we build a [CLICK] near-HBM FPGA based accelerator which is connected to a server-grade IBM POWER9-based CPU system

## Slide 141: Performance & Energy Greatly Improve
5-27× performance vs. a 16-core (64-thread) IBM POWER9 CPU
HBM alleviates memory bandwidth contention vs. DDR4
12-133× energy efficiency vs. a 16-core (64-thread) IBM POWER9 CPU
Notes: [CLICK]

## Slide 142: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 143: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 144: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 145: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 146: Potential Barriers to Adoption of PIM
1. Applications & software for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System and security support: coherence, synchronization, virtual memory, isolation, communication interfaces, …
4. Runtime and compilation systems for adaptive scheduling, data mapping, access/sharing control, …
5. Infrastructures to assess benefits and feasibility
All can be solved with change of mindset

## Slide 147: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 148: How to Keep It Simple?
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 149: How to Maintain Coherence? (I)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 150: How to Maintain Coherence? (II)
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "CoNDA: Efficient Cache Coherence Support for Near-Data Accelerators" Proceedings of the 46th International Symposium on Computer Architecture (ISCA), Phoenix, AZ, USA, June 2019.

## Slide 151: Challenge: Coherence for Hybrid CPU-PIM Apps
Traditional
coherence
No coherence
overhead

## Slide 152: How to Support Synchronization?
Christina Giannoula, Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas, Ivan Fernandez, Juan Gómez-Luna, Lois Orosa, Nectarios Koziris, Georgios Goumas, Onur Mutlu, "SynCron: Efficient Synchronization Support for Near-Data-Processing Architectures" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Short Talk Video (7 minutes)]

## Slide 153: How to Support Virtual Memory?
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 154: Eliminating the Adoption Barriers
Processing-in-Memory
in the Real World

## Slide 155: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 156: UPMEM Memory Modules
E19: 8 chips DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 157: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 158: More on the UPMEM PIM System
https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=26

## Slide 159: Experimental Analysis of the UPMEM PIM Engine
https://arxiv.org/pdf/2105.03814.pdf

## Slide 160: PrIM Benchmarks: Application Domains
Domain | Benchmark | Short name
Dense linear algebra | Vector Addition | VA
 | Matrix-Vector Multiply | GEMV
Sparse linear algebra | Sparse Matrix-Vector Multiply | SpMV
Databases | Select | SEL
 | Unique | UNI
Data analytics | Binary Search | BS
 | Time Series Analysis | TS
Graph processing | Breadth-First Search | BFS
Neural networks | Multilayer Perceptron | MLP
Bioinformatics | Needleman-Wunsch | NW
Image processing | Image histogram (short) | HST-S
 | Image histogram (large) | HST-L
Parallel primitives | Reduction | RED
 | Prefix sum (scan-scan-add) | SCAN-SSA
 | Prefix sum (reduce-scan-scan) | SCAN-RSS
 | Matrix transposition | TRNS

## Slide 161: PrIM Benchmarks are Open Source
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 162: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 163: Understanding a Modern PIM Architecture
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 164: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9

## Slide 165: More on Analysis of the UPMEM PIM Engine
https://www.youtube.com/watch?v=Pp9jSU2b9oM&list=PL5Q2soXY2Zi8_VVChACnON4sfh2bJ5IrD&index=159

## Slide 166: FPGA-based Processing Near Memory
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), to appear, 2021.

## Slide 167: DAMOV Analysis Methodology & Workloads
https://arxiv.org/pdf/2105.03725.pdf

## Slide 168: When to Employ Near-Data Processing?
Near-Data
Processing
Mobile consumer workloads
(GoogleWL2)
Neural networks
(GoogleWL2)
Graph processing
(Tesseract1)
Time series analysis
(NATSA6)
DNA
sequence mapping
(GenASM3; GRIM-Filter4)
...
[1] Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing," ISCA, 2015
[2] Boroumand+, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018
[3] Cali+, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis,” MICRO, 2020
[4] Kim+, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies,” BMC Genomics, 2018
[5] Boroumand+, "Polynesia: Enabling Effective Hybrid Transactional/Analytical Databases with Specialized Hardware/Software Co-Design,” arXiv:2103.00798 [cs.AR], 2021
[6] Fernandez+, “NATSA: A Near-Data Processing Accelerator for Time Series Analysis,” ICCD, 2020
Databases
(Polynesia5)
Notes: [CLICK] Many recent works explore how NDP can benefit various application domains like
[CLICK] Graph processing,
[CLICK] mobile consumer workloads
[CLICK] neural networks
[CLICK] DNA sequence mapping
[CLICK] Databases
[CLICK] Time series analysis
[CLICK] and more
[NEXT]

## Slide 169: Step 1: Application Profiling
We analyze 345 applications from distinct domains:
Graph Processing
Deep Neural Networks
Physics
High-Performance Computing
Genomics
Machine Learning
Databases
Data Reorganization
Image Processing
Map-Reduce
Benchmarking
Linear Algebra
…
Physics
Security
Machine learning
Database
Graph processing
Data analytics
Data reorganization
Genomics
Deep Neural Networks
Image processing
Linear algebra
Signal processing
Data mining
Notes: In this work, we analyzed 345 applications from distinct domains, from
[CLICK] GRAPH Processing [CLICK] Neural Networks
[CLICK] Physics [CLICK] High-performance computing
[CLICK]Genomics [CLICK] And more
[NEXT]

## Slide 170: Step 3: Memory Bottleneck Analysis
Temporal Locality
Low
High
LFMR
Decreasing
High
MPKI
High
AI
AI
MPKI
AI
LFMR
MPKI
MPKI
Low
Increasing
AI
AI
Low
Low
Low
Low
High
Low
Low
Low
Low
Low
1a: DRAM Bandwidth
1b: DRAM Latency
1c: L1/L2
Cache Capacity
2a: L3 Cache Contention
2c: Compute-Bound
2b: L1 Cache Capacity
Memory Bottleneck Class
  Six classes of
  data movement bottlenecks:
  each class ↔ data movement
  mitigation mechanism
Notes: [CLICK] With such classification, we analyze how the functions in each class correlates with different data movement mitigation mechanisms in terms of performance and energy using our scalability analysis.
[NEXT]

## Slide 171: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 172: DAMOV is Open Source
We open-source our benchmark suite and our toolchain
DAMOV-SIM
DAMOV
Benchmarks
Get DAMOV at:
https://github.com/CMU-SAFARI/DAMOV
Notes: We open source DAMOV to facilitate further research in mitigating data movement bottlenecks, including in near data processing.
[CLICK] In our DAMOV repository, we provide
[CLICK] The complete set of 144 application functions that compose our benchmark suite
[CLICK] And our DAMOV-SIM simulator
[NEXT]

## Slide 173: More on DAMOV Analysis Methodology & Workloads
https://www.youtube.com/watch?v=GWideVyo0nM&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9&index=3

## Slide 174: More on DAMOV Methods & Benchmarks
Geraldo F. Oliveira, Juan Gomez-Luna, Lois Orosa, Saugata Ghose, Nandita Vijaykumar, Ivan fernandez, Mohammad Sadrosadati, and Onur Mutlu, "DAMOV: A New Methodology and Benchmark Suite for Evaluating Data Movement Bottlenecks" IEEE Access, 8 September 2021. Preprint in arXiv, 8 May 2021. [arXiv preprint] [IEEE Access version] [DAMOV Suite and Simulator Source Code] [SAFARI Live Seminar Video (2 hrs 40 mins)] [Short Talk Video (21 minutes)]

## Slide 175: Samsung Function-in-Memory DRAM (2021)
https://news.samsung.com/global/samsung-develops-industrys-first-high-bandwidth-memory-with-ai-processing-power

## Slide 176: Samsung Function-in-Memory DRAM (2021)

## Slide 177: Samsung Function-in-Memory DRAM (2021)

## Slide 178: Samsung Function-in-Memory DRAM (2021)

## Slide 179: Samsung Function-in-Memory DRAM (2021)

## Slide 180: Samsung AxDIMM (2021)
DDRx-PIM
  DLRM recommendation system
Baseline System
AxDIMM System
Ke et al. "Near-Memory Processing in Action: Accelerating Personalized Recommendation with AxDIMM", IEEE Micro (2021)

## Slide 181: Future: Enable New Medical/Health Platforms
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION

## Slide 182: Future of Genome Sequencing & Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 183: Detailed Lectures on PIM (I)
Computer Architecture, Fall 2020, Lecture 6
  Computation in Memory (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=oGcZAGwfEUE&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=12
Computer Architecture, Fall 2020, Lecture 7
  Near-Data Processing (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=j2GIigqn1Qw&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=13
Computer Architecture, Fall 2020, Lecture 11a
  Memory Controllers (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=TeG773OgiMQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=20
Computer Architecture, Fall 2020, Lecture 12d
  Real Processing-in-DRAM with UPMEM (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=25
https://www.youtube.com/onurmutlulectures

## Slide 184: Detailed Lectures on PIM (II)
Computer Architecture, Fall 2020, Lecture 15
  Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=AlE1rD9G_YU&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=28
Computer Architecture, Fall 2020, Lecture 16a
  Opportunities & Challenges of Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=pmLszWGmMGQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=29
Computer Architecture, Fall 2020, Guest Lecture
  In-Memory Computing: Memory Devices & Applications (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=wNmqQHiEZNk&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=41
https://www.youtube.com/onurmutlulectures

## Slide 185: Latest Longer & Detailed Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing" Education Class at Embedded Systems Week (ESWEEK), Virtual, 9 October 2021. [Slides (pptx) (pdf)] [Abstract (pdf)] [Talk Video (2 hours, including Q&A)] [Invited Paper at DATE 2021] ["A Modern Primer on Processing in Memory" paper]
https://www.youtube.com/watch?v=N1Ac1ov1JOM
https://www.youtube.com/onurmutlulectures

## Slide 186: Latest Longer & Detailed Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing" Education Class at Embedded Systems Week (ESWEEK), Virtual, 9 October 2021. [Slides (pptx) (pdf)] [Abstract (pdf)] [Talk Video (2 hours, including Q&A)] [Invited Paper at DATE 2021] ["A Modern Primer on Processing in Memory" paper]
https://www.youtube.com/watch?v=N1Ac1ov1JOM&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=65
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=N1Ac1ov1JOM

## Slide 187: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 188: Challenge and Opportunity for Future
Fundamentally
High-Performance
(Data-Centric)
Computing Architectures

## Slide 189: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 190: Unfortunately, Little or No Time for the Next Two Parts

## Slide 191: Challenge and Opportunity for Future
Data-Driven
(Self-Optimizing)
Computing Architectures

## Slide 192: Challenge and Opportunity for Future
Data-Aware
(Expressive)
Computing Architectures

## Slide 193: More Info in This Longer Tutorial…
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 194: A Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=H3sEaINPBOE

## Slide 195: Concluding Remarks

## Slide 196: Concluding Remarks
It is time to design principled system architectures to solve the data handling (i.e., memory/storage) problem
Design complete systems to be truly balanced, high-performance, and energy-efficient  intelligent systems
  Data-centric, data-driven, data-aware
Enable computation capability inside and close to memory
This can
  Lead to orders-of-magnitude improvements
  Enable new applications & computing platforms
  Enable better understanding of nature
  …
Notes: Perhaps we have taken processor-centric system design a bit too far

## Slide 197: Fundamentally Better Architectures
Data-centric
Data-driven
Data-aware

## Slide 198
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 199: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 200: We Need to Exploit Good Principles
Data-centric system design
All components intelligent
Better (cross-layer) communication, better interfaces
Better-than-worst-case design
Heterogeneity
Flexibility, adaptability
Open minds

## Slide 201: A Blueprint for Fundamentally Better Architectures
Onur Mutlu, "Intelligent Architectures for Intelligent Computing Systems" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Virtual, February 2021. [Slides (pptx) (pdf)] [IEDM Tutorial Slides (pptx) (pdf)] [Short DATE Talk Video (11 minutes)] [Longer IEDM Tutorial Video (1 hr 51 minutes)]

## Slide 202: Funding Acknowledgments
Alibaba, AMD, ASML, Google, Facebook, Hi-Silicon, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware, Xilinx
NSF
NIH
GSRC
SRC
CyLab
EFCL

## Slide 203: Acknowledgments
Think BIG, Aim HIGH!
https://safari.ethz.ch

## Slide 204
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 205: SAFARI Newsletter December 2021 Edition
https://safari.ethz.ch/safari-newsletter-december-2021/

## Slide 206: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 207: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 208: Memory-Centric Computing
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
9 February 2022
Intel Interconnect & Connectivity Summit Keynote Speech

## Slide 209: Backup Slides

## Slide 210: System Desirables
Self-managing, independent components
All components intelligent & equal partners
Easy collaboration & partitioning across all components
Fine-grained communication of data & tasks
Seamless caching & translation & protection anywhere
Execution anywhere without rewriting code
Flexibility, adaptability, self-optimization
Open minds

## Slide 211: SAFARI Research Group

## Slide 212: SAFARI Newsletter April 2020 Edition
https://safari.ethz.ch/safari-newsletter-april-2020/

## Slide 213: SAFARI Newsletter January 2021 Edition
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 214: SAFARI Newsletter December 2021 Edition
https://safari.ethz.ch/safari-newsletter-december-2021/

## Slide 215: A Talk on Impactful Research & Teaching
https://www.youtube.com/watch?v=83tlorht7Mc&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=54

## Slide 216: An Interview on Computing Futures
https://www.youtube.com/watch?v=8ffSEKZhmvo

## Slide 217: Latest Longer & Detailed Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing" Education Class at Embedded Systems Week (ESWEEK), Virtual, 9 October 2021. [Slides (pptx) (pdf)] [Abstract (pdf)] [Talk Video (2 hours, including Q&A)] [Invited Paper at DATE 2021] ["A Modern Primer on Processing in Memory" paper]
https://www.youtube.com/watch?v=N1Ac1ov1JOM
https://www.youtube.com/onurmutlulectures

## Slide 218: Latest Longer & Detailed Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing" Education Class at Embedded Systems Week (ESWEEK), Virtual, 9 October 2021. [Slides (pptx) (pdf)] [Abstract (pdf)] [Talk Video (2 hours, including Q&A)] [Invited Paper at DATE 2021] ["A Modern Primer on Processing in Memory" paper]
https://www.youtube.com/watch?v=N1Ac1ov1JOM&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=65
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=N1Ac1ov1JOM

## Slide 219: Detailed Lectures on PIM (I)
Computer Architecture, Fall 2020, Lecture 6
  Computation in Memory (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=oGcZAGwfEUE&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=12
Computer Architecture, Fall 2020, Lecture 7
  Near-Data Processing (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=j2GIigqn1Qw&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=13
Computer Architecture, Fall 2020, Lecture 11a
  Memory Controllers (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=TeG773OgiMQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=20
Computer Architecture, Fall 2020, Lecture 12d
  Real Processing-in-DRAM with UPMEM (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=25
https://www.youtube.com/onurmutlulectures

## Slide 220: Detailed Lectures on PIM (II)
Computer Architecture, Fall 2020, Lecture 15
  Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=AlE1rD9G_YU&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=28
Computer Architecture, Fall 2020, Lecture 16a
  Opportunities & Challenges of Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=pmLszWGmMGQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=29
Computer Architecture, Fall 2020, Guest Lecture
  In-Memory Computing: Memory Devices & Applications (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=wNmqQHiEZNk&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=41
https://www.youtube.com/onurmutlulectures

## Slide 221: Comp Arch (Current)
Fall 2021 Edition:
  https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Youtube Livestream:
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings

## Slide 222: PIM Course (Current)
Fall 2021 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2021/doku.php?id=processing_in_memory
Youtube Livestream:
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings

## Slide 223
https://www.youtube.com/onurmutlulectures

## Slide 224: Data-Driven Architectures

## Slide 225: Corollaries: Architectures Today …
Architectures are terrible at dealing with data
  Designed to mainly store and move data vs. to compute
  They are processor-centric as opposed to data-centric
Architectures are terrible at taking advantage of vast amounts of data (and metadata) available to them
  Designed to make simple decisions, ignoring lots of data
  They make human-driven decisions vs. data-driven decisions
Architectures are terrible at knowing and exploiting different properties of application data
  Designed to treat all data as the same
  They make component-aware decisions vs. data-aware

## Slide 226: Exploiting Data to Design Intelligent Architectures

## Slide 227: System Architecture Design Today
Human-driven
  Humans design the policies (how to do things)
Many (too) simple, short-sighted policies all over the system
No automatic data-driven policy learning
(Almost) no learning: cannot take lessons from past actions
Can we design
fundamentally intelligent architectures?

## Slide 228: An Intelligent Architecture
Data-driven
  Machine learns the “best” policies (how to do things)
Sophisticated, workload-driven, changing, far-sighted policies
Automatic data-driven policy learning
All controllers are intelligent data-driven agents
How do we start?

## Slide 229: Self-Optimizing Memory Controllers

## Slide 230: Memory Controller
How to schedule requests to maximize system performance?
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 231: Why are Memory Controllers Difficult to Design?
Need to obey DRAM timing constraints for correctness
  There are many (50+) timing constraints in DRAM
  tWTR: Minimum number of cycles to wait before issuing a read command after a write command is issued
  tRC: Minimum number of cycles between the issuing of two consecutive activate commands to the same bank
  …
Need to keep track of many resources to prevent conflicts
  Channels, banks, ranks, data bus, address bus, row buffers, …
Need to handle DRAM refresh
Need to manage power consumption
Need to optimize performance & QoS (in the presence of constraints)
  Reordering is not simple
  Fairness and QoS needs complicates the scheduling problem
…

## Slide 232: Many Memory Timing Constraints
From Lee et al., “DRAM-Aware Last-Level Cache Writeback: Reducing Write-Caused Interference in Memory Systems,” HPS Technical Report, April 2010.

## Slide 233: Many Memory Timing Constraints
Kim et al., “A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.

## Slide 234: Memory Controller Design Is Becoming More Difficult
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
Many timing constraints for various memory types
Many goals at the same time: performance, fairness, QoS, energy efficiency, …
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories

## Slide 235: Reality and Dream
Reality: It difficult to design a policy that maximizes performance, QoS, energy-efficiency, …
  Too many things to think about
  Continuously changing workload and system behavior
Dream: Wouldn’t it be nice if the DRAM controller automatically found a good scheduling policy on its own?

## Slide 236: Self-Optimizing DRAM Controllers
Ipek+, “Self Optimizing Memory Controllers: A Reinforcement Learning Approach,” ISCA 2008.
Problem: DRAM controllers are difficult to design
  It is difficult for human designers to design a policy that can adapt itself very well to different workloads and different system conditions
Idea: A memory controller that adapts its scheduling policy to workload behavior and system conditions using machine learning.
Observation: Reinforcement learning maps nicely to memory control.
Design: Memory controller is a reinforcement learning agent
  It dynamically and continuously learns and employs the best scheduling policy to maximize long-term performance.

## Slide 237: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.
Goal: Learn to choose actions to maximize r0 + r1 + 2r2 + … ( 0   < 1)

## Slide 238: Self-Optimizing DRAM Controllers
Dynamically adapt the memory scheduling policy via interaction with the system at runtime
  Associate system states and actions (commands) with long term reward values: each action at a given state leads to a learned reward
  Schedule command with highest estimated long-term reward value in each state
  Continuously update reward values for <state, action> pairs based on feedback from system

## Slide 239: Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 240: States, Actions, Rewards
Reward function
  +1 for scheduling Read and Write commands
  0 at all other times
  Goal is to maximize long-term data bus utilization
State attributes
  Number of reads, writes, and load misses in transaction queue
  Number of pending writes and ROB heads waiting for referenced row
  Request’s relative ROB order
Actions
  Activate
  Write
  Read - load miss
  Read - store miss
  Precharge - pending
  Precharge - preemptive
  NOP

## Slide 241: Performance Results
Large, robust performance improvements over many human-designed policies

## Slide 242: Self Optimizing DRAM Controllers
+ Continuous learning in the presence of changing environment
+ Reduced designer burden in finding a good scheduling policy. Designer specifies:
1) What system variables might be useful
2) What target to optimize, but not how to optimize it
-- How to specify different objectives? (e.g., fairness, QoS, …)
-- Hardware complexity?
-- Design mindset and flow

## Slide 243: More on Self-Optimizing DRAM Controllers
Engin Ipek, Onur Mutlu, José F. Martínez, and Rich Caruana, "Self Optimizing Memory Controllers: A Reinforcement Learning Approach" Proceedings of the 35th International Symposium on Computer Architecture (ISCA), pages 39-50, Beijing, China, June 2008.

## Slide 244: Self-Optimizing Memory Prefetchers
Rahul Bera, Konstantinos Kanellopoulos, Anant Nori, Taha Shahroodi, Sreenivas Subramoney, and Onur Mutlu, "Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (1.5 minutes)] [Pythia Source Code (Officially Artifact Evaluated with All Badges)] [arXiv version]
https://arxiv.org/pdf/2109.12021.pdf

## Slide 245
Rahul Bera, Konstantinos Kanellopoulos, Anant V. Nori,
Taha Shahroodi, Sreenivas Subramoney, Onur Mutlu
Pythia
A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning
https://github.com/CMU-SAFARI/Pythia
Notes: Hi I am Rahul. Today, I’m going to present our work “…”
This work is done by researchers from SAFARI research group at ETH Zurich, in collaboration with Intel Labs and TU Delft.

## Slide 246: Executive Summary
https://github.com/CMU-SAFARI/Pythia
Background: Prefetchers predict addresses of future memory requests by associating memory access patterns with program context (called feature)
Problem: Three key shortcomings of prior prefetchers:
  Predict mainly using a single program feature
  Lack inherent system awareness (e.g., memory bandwidth usage)
  Lack in-silicon customizability
Goal: Design a prefetching framework that:
  Learns from multiple features and inherent system-level feedback
  Can be customized in silicon to use different features and/or prefetching objectives
Contribution: Pythia, which formulates prefetching as reinforcement learning problem
  Takes adaptive prefetch decisions using multiple features and system-level feedback
  Can be customized in silicon for target workloads via simple configuration registers
  Proposes a realistic and practical implementation of RL algorithm in hardware
Key Results:
  Evaluated using a wide range of workloads from SPEC CPU, PARSEC, Ligra, Cloudsuite
  Outperforms best prefetcher (in 1-core config.) by 3.4%, 7.7% and 17% in 1/4/bw-constrained cores
  Up to 7.8% more performance over basic Pythia across Ligra workloads via simple customization
Notes: First, I am going to start with an executive summary.
[CLICK] Prefetching is a speculative technique that predicts address of future memory requests by associating patterns in memory addresses with some program context. We call this context a feature.
[CLICK] We observe three key shortcomings in prior prefetchers:
First, they mainly use a single program feature for prediction.
Second, they lack inherent system awareness
Third, they also lack any customizability in silicon
[CLICK] Our goal in this work is to design a prefetching framework that
– can learn from multiple program features and inherent system-level feedback
-- and can be customized in silicon to change the features or the objective of the prefetcher
[CLICK] Towards this we propose Pythia, that formulates …
Pythia makes adaptive and autonomous …
Pythia also proposes a realistic and practical …
[CLICK] We extensively evaluate Pythia using …
We show that Pythia outperforms prior state-of-the-art …
Pythia is freely available in our GitHub repository.

## Slide 247: Key Shortcomings in Prior Prefetchers
We observe three key shortcomings that significantly limit performance benefits of prior prefetchers
Predict mainly using a single program feature
Lack inherent system awareness
Lack in-silicon customizability
1
2
3
Notes: We observe three key shortcomings in prior prefetchers that significantly limits their performance improvement
[CLICK] First, they predict mainly …
[CLICK] Second, they lack any inherent …
[CLICK] Third, the also lack any online in-silicon customizability
Let’s take a closer look at each of these shortcomings.
[NEXT]

## Slide 248: Our Goal
A prefetching framework that can:
Learn to prefetch using multiple features and inherent system-level feedback information
Be easily customized in silicon to use different features and/or change prefetcher’s objectives
Notes: So our goal in this work is to … that
[CLICK] …
[CLICK] …

## Slide 249: Our Proposal
Pythia
Formulates prefetching as a reinforcement learning problem
Pythia is named after the oracle of Delphi, who is known for her accurate prophecies
https://en.wikipedia.org/wiki/Pythia

## Slide 250: Basics of Reinforcement Learning (RL)
Algorithmic approach to learn to take an action in a given situation to maximize a numerical reward
Agent stores Q-values for every state-action pair
  Expected return for taking an action in a state
  Given a state, selects action that provides highest Q-value
Notes: First, let me briefly describe the basics of reinforcement learning.
Reinforcement learning, in its simplest form, is the ...
A RL system contains two components: [CLICK] the agent and the environment.
The agent observes the state of the environment in every timestep [CLICK], takes an action based on the state [CLICK], and receives a reward for that action [CLICK].
[CLICK] The agent stores …
Given a state, the agent …

## Slide 251: Formulating Prefetching as RL
Notes: In Pythia, we formulate prefetching as a reinforcement learning problem.
[CLICK] The prefetcher acts as the agent, while [CLICK] the processor and memory subsystem acts as the environment.
[CLICK] Pythia extracts the program features from every demand request and use it as a state information to take a prefetch action [CLICK]
[CLICK] For every prefetch action, Pythia receives a numerical reward that evaluates the usefulness of the prefetch request, while considering various system-level feedbacks.
Not let’s concretely define the state, action, and the reward for Pythia.

## Slide 252: Pythia Overview
Q-Value Store: Records Q-values for all state-action pairs
Evaluation Queue: A FIFO queue of recently-taken actions
Evaluation Queue (EQ)
Demand Request
1
Assign reward to
corresponding EQ entry
Look up
QVStore
State
Vector
Q-Value Store
(QVStore)
2
3
5
Insert prefetch action &
State-Action pair in EQ
6
Prefetch Fill
A1
A2
A3
Memory
Hierarchy
Generate
prefetch
Evict EQ entry and update QVStore
4
Find the Action with max Q-Value
7
S1
S2
S3
S4
Set filled bit
Max
Notes: Pythia consists of two key components:
[CLICK] Q-value store, which is responsible for …
[CLICK] Evaluation queue, which is a first-in-first-out queue that stores the recently taken action.
As Pythia cannot always immediately assign a reward to a taken action
because the usefulness of the corresponding prefetch request is known, Pythia stores the action
in evaluation queue to properly assign rewards to them.
[CLICK] For every demand request, Pythia first checks EQ with deamdned address. If a matching entry is found in EQ, it means the corresponding action in EQ entry has generated a useful prefetch, and Pythia assigns a reward accordingly.
[CLICK] Then Pythia extracts features from the attributes of the demand request to create the state-vector and uses the state-vector to lookup QVStore [CLICK]
[CLICK] For the given state-vector, Pythia finds the action that has the highest Q-value and generates prefetch request accordingly to the memory hierarchy [CLICK]
[CLICK] Next, Pythia inserts the action in the EQ along with the state-action pair.
[CLICK] Pythia uses the reward stored in the evicted EQ entry to update the QVStore.

## Slide 253: Simulation Methodology
Champsim [3] trace-driven simulator
150 single-core memory-intensive workload traces
  SPEC CPU2006 and CPU2017
  PARSEC 2.1
  Ligra
  Cloudsuite
Homogeneous and heterogeneous multi-core mixes
Five state-of-the-art prefetchers
  SPP [Kim+, MICRO’16]
  Bingo [Bakhshalipour+, HPCA’19]
  MLOP [Shakerinava+, 3rd Prefetching Championship, 2019 ]
  SPP+DSPatch [Bera+, MICRO’19]
  SPP+PPF [Bhatia+, ISCA’20]
[3] https://github.com/ChampSim/ChampSim

## Slide 254: Basic Pythia Configuration
Derived from automatic design-space exploration
State: 2 features
  PC+Delta
  Sequence of last-4 deltas
Actions: 16 prefetch offsets
  Ranging between -6 to +32. Including 0.
Rewards:
  RAT = +20; RAL = +12; RNP-H=-2; RNP-L=-4;
  RIN-H=-14; RIN-L=-8; RCL=-12

## Slide 255: Performance with Varying Core Count
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
Bingo
MLOP
SPP
Pythia
3.4%
7.7%

## Slide 256: Performance with Varying Core Count
Chart: Number of cores
| 1 | 2 | 4 | 6 | 8 | 12
SPP | 1.1809 | 1.2748 | 1.2361 | 1.2322 | 1.2107 | 1.1844
Bingo | 1.1861 | 1.2832 | 1.2186 | 1.1864 | 1.1783 | 1.1578
MLOP | 1.1902 | 1.2833 | 1.2429 | 1.231 | 1.2074 | 1.1769
Pythia | 1.2242 | 1.3243 | 1.3009 | 1.2853 | 1.2704 | 1.2538
Bingo
MLOP
SPP
Pythia
3.4%
7.7%
1. Pythia consistently provides the highest performance in all core configurations
2. Pythia’s gain increases with core count

## Slide 257: Performance with Varying DRAM Bandwidth
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
SPP | 0.97243 | 1.0879 | 1.1469 | 1.1722 | 1.1809 | 1.183 | 1.1839
Bingo | 0.80726 | 0.93831 | 1.052 | 1.1432 | 1.1861 | 1.199 | 1.2005
MLOP | 0.84028 | 0.99928 | 1.1044 | 1.1689 | 1.1902 | 1.196 | 1.1975
Pythia | 1.009 | 1.1308 | 1.1837 | 1.2142 | 1.2242 | 1.2265 | 1.2278
~Intel Xeon 6258R
~AMD EPYC Rome 7702P
~AMD Threadripper 3990x
SPP
Bingo
MLOP
Pythia
Baseline
3%
17%

## Slide 258: Performance with Varying DRAM Bandwidth
Chart: DRAM MTPS (in log scale)
| 150 | 300 | 600 | 1200 | 2400 | 4800 | 9600
SPP | 0.97243 | 1.0879 | 1.1469 | 1.1722 | 1.1809 | 1.183 | 1.1839
Bingo | 0.80726 | 0.93831 | 1.052 | 1.1432 | 1.1861 | 1.199 | 1.2005
MLOP | 0.84028 | 0.99928 | 1.1044 | 1.1689 | 1.1902 | 1.196 | 1.1975
Pythia | 1.009 | 1.1308 | 1.1837 | 1.2142 | 1.2242 | 1.2265 | 1.2278
~Intel Xeon 6258R
~AMD EPYC Rome 7702P
~AMD Threadripper 3990x
SPP
Bingo
MLOP
Pythia
Baseline
3%
17%
Pythia outperforms prior best prefetchers for
a wide range of DRAM bandwidth configurations

## Slide 259: Pythia’s Overhead
25.5 KB of total metadata storage per core
  Only simple tables
We also model functionally-accurate Pythia with full complexity in Chisel [4] HDL
1.03% area overhead
Satisfies prediction latency
0.4% power overhead
of a desktop-class 4-core Skylake processor (Xeon D2132IT, 60W)
[4] https://www.chisel-lang.org
Notes: All of Pythia’s performance benefits comes at a modest cost of 25.5KB of metadata storge, which is invested only in simple storage, without any need to complex structures.
[CLICK] We also model a fully-functionally-accurate Pythia with its full complexity in Chisel and show that, Pythia incurs
[CLICK] a modest area overhead of 1.03%
[CLICK] a power overhead of half-a-percent
[CLICK] while simultaneously satisfying the prediction latency at L2 cache frequency
Of a desktop-class …

## Slide 260: More in the Paper
Performance comparison with unseen traces
  Pythia provides equally high performance benefits
Comparison against multi-level prefetchers
  Pythia outperforms prior best multi-level prefetchers
Understanding Pythia’s learning with a case study
  We reason towards the correctness of Pythia’s decision
Performance sensitivity towards different features and hyperparameter values
Detailed single-core and four-core performance
https://arxiv.org/pdf/2109.12021.pdf
Notes: We have many more exciting results including, ….
We encourage everyone to read it.

## Slide 261: Pythia is Open Source
https://github.com/CMU-SAFARI/Pythia
MICRO’21 artifact evaluated
Champsim source code + Chisel modeling code
All traces used for evaluation

## Slide 262
Rahul Bera, Konstantinos Kanellopoulos, Anant V. Nori,
Taha Shahroodi, Sreenivas Subramoney, Onur Mutlu
Pythia
A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning
https://github.com/CMU-SAFARI/Pythia
Notes: Hi I am Rahul. Today, I’m going to present our work “…”
This work is done by researchers from SAFARI research group at ETH Zurich, in collaboration with Intel Labs and TU Delft.

## Slide 263: Self-Optimizing Memory Prefetchers
Rahul Bera, Konstantinos Kanellopoulos, Anant Nori, Taha Shahroodi, Sreenivas Subramoney, and Onur Mutlu, "Pythia: A Customizable Hardware Prefetching Framework Using Online Reinforcement Learning" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (1.5 minutes)] [Pythia Source Code (Officially Artifact Evaluated with All Badges)] [arXiv version]
https://arxiv.org/pdf/2109.12021.pdf

## Slide 264: An Intelligent Architecture
Data-driven
  Machine learns the “best” policies (how to do things)
Sophisticated, workload-driven, changing, far-sighted policies
Automatic data-driven policy learning
All controllers are intelligent data-driven agents
We need to rethink design
(of all controllers)

## Slide 265: Challenge and Opportunity for Future
Data-Driven
(Self-Optimizing)
Computing Architectures

## Slide 266: Data-Aware Architectures

## Slide 267: Corollaries: Architectures Today …
Architectures are terrible at dealing with data
  Designed to mainly store and move data vs. to compute
  They are processor-centric as opposed to data-centric
Architectures are terrible at taking advantage of vast amounts of data (and metadata) available to them
  Designed to make simple decisions, ignoring lots of data
  They make human-driven decisions vs. data-driven decisions
Architectures are terrible at knowing and exploiting different properties of application data
  Designed to treat all data as the same
  They make component-aware decisions vs. data-aware

## Slide 268: Data-Aware Architectures
A data-aware architecture understands what it can do with and to each piece of data
It makes use of different properties of data to improve performance, efficiency and other metrics
  Compressibility
  Approximability
  Locality
  Sparsity
  Criticality for Computation X
  Access Semantics
  …

## Slide 269: One Problem: Limited Expressiveness

## Slide 270: A Solution: More Expressive Interfaces

## Slide 271: Expressive (Memory) Interfaces
Nandita Vijaykumar, Abhilasha Jain, Diptesh Majumdar, Kevin Hsieh, Gennady Pekhimenko, Eiman Ebrahimi, Nastaran Hajinazar, Phillip B. Gibbons and Onur Mutlu, "A Case for Richer Cross-layer Abstractions: Bridging the Semantic Gap with Expressive Memory" Proceedings of the 45th International Symposium on Computer Architecture (ISCA), Los Angeles, CA, USA, June 2018. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video]

## Slide 272: SW provides key program information to HW
Data Structures
Access Patterns
Integer
Float
Char
Data Type/Layout
Hardware
Software
Prefetcher
Data Compression
Data Placement
Notes: But a lot of this information that HW is trying to infer is easily available to SW and with a richer interface that conveys a higher-level program information we can enable the system and architecture to distinguish between data structures, inform it about how these data structures are accessed, the data types they contain, etc. and many other things. This could help in HW optimization, for example the knowledge of data structures and their access semantics could help avoid bank conflicts in data placement or help hardware prefetchers. Knowledge of data types could help in data compression engines.

## Slide 273: Broader goal: Enable many cross-layer optimizations
Optimizations:
Cache Management
Data Placement in DRAM
Data Compression
Approximation
DRAM Cache Management
NVM Management
NUCA/NUMA Optimizations
…
Express:
Data structures
Access semantics
Data types
Working set
Reuse
Access frequency
…
Benefits:
More efficient HW:
Performance
Reduced SW burden:
Programmability
Portability

## Slide 274: Our approach: Rich cross-layer abstractions
Cross-layer Abstraction + Interfaces
Generality: Enable a wide range of cross-layer approaches
Minimize programmer effort
Overhead
Program
Caches
Memory
Controller
OS
Prefetcher
Driver
Compiler
Approach: Flexibly associate specific semantic information with any data & code
Expressive Memory
“XMem”

## Slide 275
Example: XMem
Goal: convey data semantics to the hardware enables more intelligent management of resources.
XMem: introduces a new HW/SW abstraction, called Atom, for conveying data semantics
275
Software
Hardware
Atom:1
Application
Atom: 2
Atom: 3
System/Architecture
Memory
Region
Memory
Region
Memory
Region
A = malloc ( size );
Atom1 = CreateAtom( “INT”, “Regular”, …);
MapAtom( Atom1, A, size );
Vijaykumar+, “A Case for Richer Cross-layer Abstractions: Bridging the Semantic Gap with Expressive Memory”, ISCA 2018
Notes: Expressive Memory (XMem) [41] shows that conveying higher-level data structure seman-tics to various system components including hardware enables the system to better managethe underlying resources.
[CLICK] To do this, XMem extends existing virtual memory frameworks to support a new abstraction, called Atom.
[CLICK[ To convey access properties of a virtual address region, the application is expected to create a new Atom for the region and associate the Atom with the corresponding properties.
[CLICK] here is an example of how an application uses atom to express program semantics. After malloc, the atom is created with the desired properties, and then, the atom is mapped to the allocated region in the virtual memory
Xmem creates a separate pathway to communicate information about Atoms to the OS and the hardware.

## Slide 276: XMem Aids/Enables Many Optimizations

## Slide 277: Expressive (Memory) Interfaces
Nandita Vijaykumar, Abhilasha Jain, Diptesh Majumdar, Kevin Hsieh, Gennady Pekhimenko, Eiman Ebrahimi, Nastaran Hajinazar, Phillip B. Gibbons and Onur Mutlu, "A Case for Richer Cross-layer Abstractions: Bridging the Semantic Gap with Expressive Memory" Proceedings of the 45th International Symposium on Computer Architecture (ISCA), Los Angeles, CA, USA, June 2018. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video]

## Slide 278: Expressive (Memory) Interfaces for GPUs
Nandita Vijaykumar, Eiman Ebrahimi, Kevin Hsieh, Phillip B. Gibbons and Onur Mutlu, "The Locality Descriptor: A Holistic Cross-Layer Abstraction to Express Data Locality in GPUs" Proceedings of the 45th International Symposium on Computer Architecture (ISCA), Los Angeles, CA, USA, June 2018. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video]

## Slide 279: Locality Descriptor: Executive Summary
Exploiting data locality in GPUs is a challenging task
Software
Hardware
Locality Descriptor
Cache Management
CTA Scheduling
Data Placement
Data Prefetching
…
Application
Flexible, architecture-agnostic interface
Access to program semantics
Performance Benefits:
26.6% (up to 46.6%) from cache locality
53.7% (up to 2.8x) from NUMA locality

## Slide 280: An Example: Hybrid Memory Management
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
SoC
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 281: An Example: Heterogeneous-Reliability Memory
Yixin Luo, Sriram Govindan, Bikash Sharma, Mark Santaniello, Justin Meza, Aman Kansal, Jie Liu, Badriddine Khessib, Kushagra Vaid, and Onur Mutlu, "Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost via Heterogeneous-Reliability Memory" Proceedings of the 44th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Atlanta, GA, June 2014. [Summary] [Slides (pptx) (pdf)] [Coverage on ZDNet]

## Slide 282: Exploiting Memory Error Tolerance with Hybrid Memory Systems
Chart: Memory error vulnerability
| App/Data A | App/Data B | App/Data C
System/Application Crash | 1.0414 | 0.63898 | 0.24773
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory [DSN 2014]
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search workload
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 283: Heterogeneous-Reliability Memory
App 1 data A
App 1 data B
App 2 data A
App 2 data B
App 3 data A
App 3 data B
Step 2: Map application data to the HRM system enabled by SW/HW cooperative solutions
Step 1: Characterize and classify application memory error tolerance
Reliable memory
Parity memory + software recovery (Par+R)
Low-cost memory
Unreliable
Reliable
Vulnerable
Tolerant
App 1 data A
App 2 data A
App 2 data B
App 3 data A
App 3 data B
App 1 data B
Notes: Now we have described the key idea of HRM and Par+R, let’s look at our mechanism to put them together.
First, we characterize and classify application data in terms of their memory error tolerance, rank them from vulnerable to tolerant.
Then, we map application data to HRM according to their error tolerance. As an example here, vulnerable data is mapped to reliable memory, tolerable data is mapped to low-cost memory, and recoverable data is mapped to parity memory with Par+R.

## Slide 284: More on Heterogeneous-Reliability Memory
Yixin Luo, Sriram Govindan, Bikash Sharma, Mark Santaniello, Justin Meza, Aman Kansal, Jie Liu, Badriddine Khessib, Kushagra Vaid, and Onur Mutlu, "Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost via Heterogeneous-Reliability Memory" Proceedings of the 44th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Atlanta, GA, June 2014. [Summary] [Slides (pptx) (pdf)] [Coverage on ZDNet]

## Slide 285: Data-Aware Cross-Layer Hybrid System Management
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
Many timing constraints for various memory types
Many goals at the same time: performance, fairness, QoS, energy efficiency, …
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories

## Slide 286: Another Example: EDEN for DNNs
Deep Neural Network evaluation is very DRAM-intensive (especially for large networks)
1. Some data and layers in DNNs are very tolerant to errors
2. Reduce DRAM latency and voltage on such data and layers
3. While still achieving a user-specified DNN accuracy target by making training DRAM-error-aware
Data-aware management of DRAM latency and voltage for Deep Neural Network Inference

## Slide 287
Mapping example of ResNet-50:
Example DNN Data Type to DRAM Mapping
Map more error-tolerant DNN layers
to DRAM partitions with lower voltage/latency
1
2
3
4
<2% BER
<5% BER
<6% BER
<8% BER
4 DRAM partitions with different error rates
Notes: In contrast, using a DRAM chip partitioned into four voltage domains can use a many-to-four DNN to DRAM mapping, using four different voltage values with error rates indicated by the yellow, red, green, and blue lines

## Slide 288
Key idea: Enable accurate, efficient DNN inference using approximate DRAM
EDEN is an iterative process that has 3 key steps
EDEN: Overview
Notes: To exploit these two insights, we propose EDEN: a framework to enable accurate DNN inference on approximate DRAM through three key steps;
1) boosting DNN error tolerance, 2) DNN and DRAM error tolerance characterization, and 3) DNN-DRAM mapping.
These steps are repeated iteratively until EDEN finds the most aggressive configuration that meets the target accuracy requirements

## Slide 289
CPU: DRAM Energy Evaluation
Average 21% DRAM energy reduction
maintaining accuracy within 1% of original

## Slide 290
Average 8% system speedup
Some workloads achieve 17% speedup
CPU: Performance Evaluation
EDEN achieves close to the ideal speedup
possible via tRCD scaling
Ideal

## Slide 291
GPU, Eyeriss, and TPU: Energy Evaluation
GPU: average 37% energy reduction
Eyeriss: average 31% energy reduction
TPU: average 32% energy reduction

## Slide 292: EDEN: Data-Aware Efficient DNN Inference
Skanda Koppula, Lois Orosa, A. Giray Yaglikci, Roknoddin Azizi, Taha Shahroodi, Konstantinos Kanellopoulos, and Onur Mutlu, "EDEN: Enabling Energy-Efficient, High-Performance Deep Neural Network Inference Using Approximate DRAM" Proceedings of the 52nd International Symposium on Microarchitecture (MICRO), Columbus, OH, USA, October 2019. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 293: SMASH: SW/HW Indexing Acceleration
Konstantinos Kanellopoulos, Nandita Vijaykumar, Christina Giannoula, Roknoddin Azizi, Skanda Koppula, Nika Mansouri Ghiasi, Taha Shahroodi, Juan Gomez-Luna, and Onur Mutlu, "SMASH: Co-designing Software Compression and Hardware-Accelerated Indexing for Efficient Sparse Matrix Operations" Proceedings of the 52nd International Symposium on Microarchitecture (MICRO), Columbus, OH, USA, October 2019. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Lightning Talk Video (90 seconds)] [Full Talk Lecture (30 minutes)]

## Slide 294: Data-Aware Virtual Memory Framework
Nastaran Hajinazar, Pratyush Patel, Minesh Patel, Konstantinos Kanellopoulos, Saugata Ghose, Rachata Ausavarungnirun, Geraldo Francisco de Oliveira Jr., Jonathan Appavoo, Vivek Seshadri, and Onur Mutlu, "The Virtual Block Interface: A Flexible Alternative to the Conventional Virtual Memory Framework" Proceedings of the 47th International Symposium on Computer Architecture (ISCA), Virtual, June 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [ARM Research Summit Poster (pptx) (pdf)] [Talk Video (26 minutes)] [Lightning Talk Video (3 minutes)] [Lecture Video (43 minutes)]

## Slide 295: SW/HW Climate Modeling Accelerator
Gagandeep Singh, Dionysios Diamantopoulos, Christoph Hagleitner, Juan Gómez-Luna, Sander Stuijk, Onur Mutlu, and Henk Corporaal, "NERO: A Near High-Bandwidth Memory Stencil Accelerator for Weather Prediction Modeling" Proceedings of the 30th International Conference on Field-Programmable Logic and Applications (FPL), Gothenburg, Sweden, September 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (23 minutes)] Nominated for the Stamatis Vassiliadis Memorial Award.

## Slide 296: HW/SW Time Series Analysis Accelerator
Ivan Fernandez, Ricardo Quislant, Christina Giannoula, Mohammed Alser, Juan Gómez-Luna, Eladio Gutiérrez, Oscar Plata, and Onur Mutlu, "NATSA: A Near-Data Processing Accelerator for Time Series Analysis" Proceedings of the 38th IEEE International Conference on Computer Design (ICCD), Virtual, October 2020. [Slides (pptx) (pdf)] [Talk Video (10 minutes)] [Source Code]

## Slide 297: FPGA-based Processing Near Memory
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), 2021.

## Slide 298: Accelerating Linked Data Structures
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 299: Accelerating Approximate String Matching
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 300: Accelerating Genome Analysis [IEEE MICRO 2020]
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 301: Challenge and Opportunity for Future
Data-Aware
(Expressive)
Computing Architectures

## Slide 302: We Need to Rethink the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there case by case

## Slide 303: Principled Architectures & What They Can Enable

## Slide 304: A Quote from A Famous Architect
“architecture […] based upon principle, and not upon precedent”

## Slide 305: Precedent-Based Design?
“architecture […] based upon principle, and not upon precedent”

## Slide 306: Principled Design
“architecture […] based upon principle, and not upon precedent”

## Slide 308: The Overarching Principle

## Slide 309: Another Example: Precedent-Based Design
Source: http://cookiemagik.deviantart.com/art/Train-station-207266944

## Slide 310: Principled Design
Source: By Toni_V, CC BY-SA 2.0, https://commons.wikimedia.org/w/index.php?curid=4087256

## Slide 311: Another Principled Design
Source: By Martín Gómez Tagle - Lisbon, Portugal, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=13764903
Source: http://www.arcspace.com/exhibitions/unsorted/santiago-calatrava/

## Slide 312: Another Principled Design
Source: CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=172107

## Slide 313: Principle Applied to Another Structure
Source: https://www.dezeen.com/2016/08/29/santiago-calatrava-oculus-world-trade-center-transportation-hub-new-york-photographs-hufton-crow/
Source: By 準建築人手札網站 Forgemind ArchiMedia - Flickr: IMG_2489.JPG, CC BY 2.0,
https://commons.wikimedia.org/w/index.php?curid=31493356, https://en.wikipedia.org/wiki/Santiago_Calatrava

## Slide 314: The Overarching Principle

## Slide 315: Overarching Principles for Computing?
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 316: Readings, Videos, Reference Materials

## Slide 317: More on My Research & Teaching

## Slide 318: Brief Self Introduction
Onur Mutlu
  Full Professor @ ETH Zurich ITET (INFK), since September 2015
  Strecker Professor @ Carnegie Mellon University ECE/CS, 2009-2016, 2016-…
  PhD from UT-Austin, worked at Google, VMware, Microsoft Research, Intel, AMD
  https://people.inf.ethz.ch/omutlu/
  omutlu@gmail.com (Best way to reach me)
  https://people.inf.ethz.ch/omutlu/projects.htm
Research and Teaching in:
  Computer architecture, computer systems, hardware security, bioinformatics
  Memory and storage systems
  Hardware security, safety, predictability
  Fault tolerance
  Hardware/software cooperation
  Architectures for bioinformatics, health, medicine
  …

## Slide 319: Current Research Mission
Computer architecture, HW/SW, systems, bioinformatics, security
Graphics and Vision Processing
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
Build fundamentally better architectures
Notes: Professor Mutlu’s research focus is all aspects of computer architecture, HW/SW interaction and bioinformatics.
He is looking for students to perform research in these areas.
He and his group, SAFARI, solve fundamental problems spanning:
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
His group does broad research spanning systems to logic with architecture at center

## Slide 320: Four Key Current Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency and Predictable Architectures
Architectures for AI/ML, Genomics, Medicine, Health

## Slide 321: The Transformation Hierarchy
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (narrow view)
Computer Architecture (expanded view)

## Slide 322: Axiom
To achieve the highest energy efficiency and performance:
we must take the expanded view
of computer architecture
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Co-design across the hierarchy:
Algorithms to devices
Specialize as much as possible
within the design goals

## Slide 323: Current Research Mission & Major Topics
Data-centric arch. for low energy & high perf.
  Proc. in Mem/DRAM, NVM, unified mem/storage
Low-latency & predictable architectures
  Low-latency, low-energy yet low-cost memory
  QoS-aware and predictable memory systems
Fundamentally secure/reliable/safe arch.
  Tolerating all bit flips; patchable HW; secure mem
Architectures for ML/AI/Genomics/Health/Med
  Algorithm/arch./logic co-design; full heterogeneity
Data-driven and data-aware architectures
  ML/AI-driven architectural controllers and design
  Expressive memory and expressive systems
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Build fundamentally better architectures
Broad research
spanning apps, systems, logic
with architecture at the center

## Slide 324
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-april-2020/

## Slide 325: SAFARI Newsletter April 2020 Edition
https://safari.ethz.ch/safari-newsletter-april-2020/

## Slide 326: SAFARI Newsletter January 2021 Edition
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 327: SAFARI Newsletter December 2021 Edition
https://safari.ethz.ch/safari-newsletter-december-2021/

## Slide 328: Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 329: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 330: SAFARI PhD and Post-Doc Alumni
https://safari.ethz.ch/safari-alumni/
Minesh Patel (ETH Zurich), MICRO 2020 and DSN 2020 Best Paper Awards; ISCA Hall of Fame 2021
Damla Senol Cali (Bionano Genomics), SRC TECHCON 2019 Best Student Presentation Award
Nastaran Hajinazar (ETH Zurich)
Gagandeep Singh (ETH Zurich), FPL 2020 Best Paper Award Finalist
Amirali Boroumand (Stanford Univ  Google), SRC TECHCON 2018 Best Student Presentation Award
Jeremie Kim (ETH Zurich), EDAA Outstanding Dissertation Award 2020; IEEE Micro Top Picks 2019; ISCA/MICRO HoF 2021
Nandita Vijaykumar (Univ. of Toronto, Assistant Professor), ISCA Hall of Fame 2021
Kevin Hsieh (Microsoft Research, Senior Researcher)
Justin Meza (Facebook), HiPEAC 2015 Best Student Presentation Award; ICCD 2012 Best Paper Award
Mohammed Alser (ETH Zurich), IEEE Turkey Best PhD Thesis Award 2018
Yixin Luo (Google), HPCA 2015 Best Paper Session
Kevin Chang (Facebook), SRC TECHCON 2016 Best Student Presentation Award
Rachata Ausavarungnirun (KMUNTB, Assistant Professor), NOCS 2015 and NOCS 2012 Best Paper Award Finalist
Gennady Pekhimenko (Univ. of Toronto, Assistant Professor), ISCA Hall of Fame 2021; ASPLOS 2015 SRC Winner
Vivek Seshadri (Microsoft Research)
Donghyuk Lee (NVIDIA Research, Senior Researcher), HPCA Hall of Fame 2018
Yoongu Kim (Software Robotics  Google), TCAD’19 Top Pick Award; IEEE Micro Top Picks’10; HPCA’10 Best Paper Session
Lavanya Subramanian (Intel Labs  Facebook)
Samira Khan (Univ. of Virginia, Assistant Professor), HPCA 2014 Best Paper Session
Saugata Ghose (Univ. of Illinois, Assistant Professor), DFRWS-EU 2017 Best Paper Award
Jawad Haj-Yahya (Huawei Research Zurich, Principal Researcher)

## Slide 331: Principle: Teaching and Research
…
Teaching drives Research
Research drives Teaching
…

## Slide 332: Principle: Learning and Scholarship
Focus on
learning and scholarship

## Slide 333: Principle: Insight and Ideas
Focus on Insight
Encourage New Ideas

## Slide 334: Principle: Learning and Scholarship
The quality of your work defines your impact

## Slide 335: Principle: Good Mindset, Goals & Focus
You can make a good impact on the world

## Slide 336: Research & Teaching: Some Overview Talks
https://www.youtube.com/onurmutlulectures
Future Computing Architectures
  https://www.youtube.com/watch?v=kgiZlSOcGFM&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=1
Enabling In-Memory Computation
  https://www.youtube.com/watch?v=njX_14584Jw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=16
Accelerating Genome Analysis
  https://www.youtube.com/watch?v=r7sn41lH-4A&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=41
Rethinking Memory System Design
  https://www.youtube.com/watch?v=F7xZLNMIY1E&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=3
Intelligent Architectures for Intelligent Machines
  https://www.youtube.com/watch?v=c6_LgzuNdkw&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=25
The Story of RowHammer
  https://www.youtube.com/watch?v=sgd7PHQQ1AI&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=39

## Slide 337: Online Courses & Lectures
First Computer Architecture & Digital Design Course
  Digital Design and Computer Architecture
  Spring 2021 Livestream Edition: https://www.youtube.com/watch?v=LbC0EZY8yw4&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN
Advanced Computer Architecture Course
  Computer Architecture
  Fall 2021 Livestream Edition: https://www.youtube.com/watch?v=c3mPdZA-Fmc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN
  Fall 2020 Edition: https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
https://www.youtube.com/onurmutlulectures

## Slide 338
https://www.youtube.com/onurmutlulectures

## Slide 339: DDCA (Spring 2021)
https://safari.ethz.ch/digitaltechnik/spring2021/doku.php?id=schedule
https://www.youtube.com/watch?v=LbC0EZY8yw4&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN
Bachelor’s course
  2nd semester at ETH Zurich
  Rigorous introduction into “How Computers Work”
  Digital Design/Logic
  Computer Architecture
  10 FPGA Lab Assignments

## Slide 340: Comp Arch (Fall 2020)
https://safari.ethz.ch/architecture/fall2020/doku.php?id=schedule
https://www.youtube.com/watch?v=c3mPdZA-Fmc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings

## Slide 341: Comp Arch (Current)
https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Youtube Livestream:
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings

## Slide 342: Seminar (Spring’21)
https://safari.ethz.ch/architecture_seminar/spring2021/doku.php?id=schedule
https://www.youtube.com/watch?v=t3m93ZpLOyw&list=PL5Q2soXY2Zi_awYdjmWVIUegsbY7TPGW4
Critical analysis course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  20+ research papers, presentations, analyses

## Slide 343: Seminar (Current)
https://safari.ethz.ch/architecture_seminar/fall2021/doku.php?id=schedule
Youtube Livestream:
  https://www.youtube.com/watch?v=4TcP297mdsI&list=PL5Q2soXY2Zi_7UBNmC9B8Yr5JSwTG9yH4
Critical analysis course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  20+ research papers, presentations, analyses

## Slide 344: Hands-On Projects & Seminars Courses
https://safari.ethz.ch/projects_and_seminars/doku.php

## Slide 345: PIM Course (Current)
Fall 2021 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2021/doku.php?id=processing_in_memory
Youtube Livestream:
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings

## Slide 346: SAFARI Live Seminars (I)
https://safari.ethz.ch/safari-seminar-series/

## Slide 347: SAFARI Live Seminars (II)
https://www.youtube.com/watch?v=D8Hjy2iU9l4&list=PL5Q2soXY2Zi_tOTAYm--dYByNPL7JhwR9&index=1

## Slide 348: Open-Source Artifacts
https://github.com/CMU-SAFARI

## Slide 349: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 350
https://github.com/CMU-SAFARI

## Slide 351: An Interview on Research and Education
Computing Research and Education (@ ISCA 2019)
  https://www.youtube.com/watch?v=8ffSEKZhmvo&list=PL5Q2soXY2Zi_4oP9LdL3cc8G6NIjD2Ydz
Maurice Wilkes Award Speech (10 minutes)
  https://www.youtube.com/watch?v=tcQ3zZ3JpuA&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=15

## Slide 352: More Thoughts and Suggestions
Onur Mutlu, "Some Reflections (on DRAM)" Award Speech for ACM SIGARCH Maurice Wilkes Award, at the ISCA Awards Ceremony, Phoenix, AZ, USA, 25 June 2019. [Slides (pptx) (pdf)] [Video of Award Acceptance Speech (Youtube; 10 minutes) (Youku; 13 minutes)] [Video of Interview after Award Acceptance (Youtube; 1 hour 6 minutes) (Youku; 1 hour 6 minutes)] [News Article on "ACM SIGARCH Maurice Wilkes Award goes to Prof. Onur Mutlu"]
Onur Mutlu, "How to Build an Impactful Research Group" 57th Design Automation Conference Early Career Workshop (DAC), Virtual, 19 July 2020. [Slides (pptx) (pdf)]

## Slide 353: More Thoughts and Suggestions (II)
Onur Mutlu, "Computer Architecture: Why Is It So Important and Exciting Today?" Invited Lecture at Izmir Institute of Technology (IYTE) , Virtual, 16 October 2020. [Slides (pptx) (pdf)] [Talk Video (2 hours 12 minutes)]
Onur Mutlu, "Applying to Graduate School & Doing Impactful Research" Invited Panel Talk at the 3rd Undergraduate Mentoring Workshop, held with the 48th International Symposium on Computer Architecture (ISCA), Virtual, 18 June 2021. [Slides (pptx) (pdf)] [Talk Video (50 minutes)]

## Slide 354: A Talk on Impactful Research & Teaching
https://www.youtube.com/watch?v=83tlorht7Mc&list=PL5Q2soXY2Zi8D_5MGV6EnXEJHnV2YFBJl&index=54

## Slide 355: An Interview on Computing Futures
https://www.youtube.com/watch?v=8ffSEKZhmvo

## Slide 356: Papers, Talks, Videos, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 357: Fundamental Thinking

## Slide 358: Historical: Opportunities at the Bottom
https://en.wikipedia.org/wiki/There%27s_Plenty_of_Room_at_the_Bottom

## Slide 359: Historical: Opportunities at the Bottom (II)
https://en.wikipedia.org/wiki/There%27s_Plenty_of_Room_at_the_Bottom

## Slide 360: Historical: Opportunities at the Top
https://science.sciencemag.org/content/368/6495/eaam9744

## Slide 361: Axiom, Revisited
There is plenty of room both at the top and at the bottom
but much more so
when you
communicate well between and optimize across
the top and the bottom

## Slide 362: Hence the Expanded View
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (expanded view)

## Slide 363: Fundamentally Better Architectures
Data-centric
Data-driven
Data-aware

## Slide 364: End of Backup Slides