## Slide 1: Rethinking Memory System Design (and the Platforms We Design Around It)
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
December 4, 2017
INESC-ID Distinguished Lecture (Lisbon)

## Slide 2: Current Research Focus Areas
Research Focus: Computer architecture, HW/SW, bioinformatics
Memory and storage (DRAM, flash, emerging), interconnects
Heterogeneous & parallel systems, GPUs, systems for data analytics
System/architecture interaction, new execution models, new interfaces
Energy efficiency, fault tolerance, hardware security, performance
Genome sequence analysis & assembly algorithms and architectures
Biologically inspired systems & system design for bio/medicine
Graphics and Vision Processing
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
Broad research
spanning apps, systems, logic
with architecture at the center
Notes: Professor Mutlu’s research focus is all aspects of computer architecture, HW/SW interaction and bioinformatics.
He is looking for students to perform research in these areas.
He and his group, SAFARI, solve fundamental problems spanning:
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
His group does broad research spanning systems to logic with architecture at center

## Slide 3: Four Key Current Directions
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency Architectures
Architectures for Genomics, Medicine, Health

## Slide 4: In-Memory DNA Sequence Analysis
Jeremie S. Kim, Damla Senol Cali, Hongyi Xin, Donghyuk Lee, Saugata Ghose, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "GRIM-Filter: Fast Seed Location Filtering in DNA Read Mapping Using Processing-in-Memory Technologies" to appear in BMC Genomics, 2018. to also appear in Proceedings of the 16th Asia Pacific Bioinformatics Conference (APBC), Yokohama, Japan, January 2018. arxiv.org Version (pdf)

## Slide 5: New Genome Sequencing Technologies

## Slide 6: Rethinking Memory & Storage

## Slide 7: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processors
and caches
Main Memory
Storage (SSD/HDD)

## Slide 8: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
FPGAs

## Slide 9: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
GPUs

## Slide 10: Memory System: A Shared Resource View
Storage
Most of the system is dedicated to storing and moving data

## Slide 11: State of the Main Memory System
Recent technology, architecture, and application trends
  lead to new requirements
  exacerbate old requirements
DRAM and memory controllers, as we know them today, are (will be) unlikely to satisfy all requirements
Some emerging non-volatile memory technologies (e.g., PCM) enable new opportunities: memory+storage merging
We need to rethink the main memory system
  to fix DRAM issues and enable emerging technologies
  to satisfy all requirements

## Slide 12: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 13: Major Trends Affecting Main Memory (II)
Need for main memory capacity, bandwidth, QoS increasing
  Multi-core: increasing number of cores/agents
  Data-intensive applications: increasing demand/hunger for data
  Consolidation: cloud computing, GPUs, mobile, heterogeneity
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 14: Example: The Memory Capacity Gap
Memory capacity per core expected to drop by 30% every two years
Trends worse for memory bandwidth per core!
Core count doubling ~ every 2 years
DRAM DIMM capacity doubling ~ every 3 years
Lim et al., ISCA 2009

## Slide 15: Example: Memory Bandwidth & Latency
Chart: DRAM Improvement (log)
| 1999.0 | 2003.0 | 2006.0 | 2008.0 | 2011.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 16: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 17: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 18: Major Trends Affecting Main Memory (III)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
  ~40-50% energy spent in off-chip memory hierarchy [Lefurgy, IEEE Computer’03] >40% power in DRAM [Ware, HPCA’10][Paul,ISCA’15]
  DRAM consumes power even when not used (periodic refresh)
DRAM technology scaling is ending

## Slide 19: Major Trends Affecting Main Memory (IV)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending
  ITRS projects DRAM will not scale easily below X nm
  Scaling has provided many benefits:
    higher capacity (density), lower cost, lower energy

## Slide 20: Major Trends Affecting Main Memory (V)
DRAM scaling has already become increasingly difficult
  Increasing cell leakage current, reduced cell reliability, increasing manufacturing difficulties [Kim+ ISCA 2014], [Liu+ ISCA 2013], [Mutlu IMW 2013], [Mutlu DATE 2017]
  Difficult to significantly improve capacity, energy
Emerging memory technologies are promising
3D-Stacked DRAM | higher bandwidth | smaller capacity
Reduced-Latency DRAM (e.g., RLDRAM, TL-DRAM) | lower latency | higher cost
Low-Power DRAM (e.g., LPDDR3, LPDDR4) | lower power | higher latency higher cost
Non-Volatile Memory (NVM) (e.g., PCM, STTRAM, ReRAM, 3D Xpoint) | larger capacity | higher latency higher dynamic power lower endurance

## Slide 21: Major Trends Affecting Main Memory (V)
DRAM scaling has already become increasingly difficult
  Increasing cell leakage current, reduced cell reliability, increasing manufacturing difficulties [Kim+ ISCA 2014], [Liu+ ISCA 2013], [Mutlu IMW 2013], [Mutlu DATE 2017]
  Difficult to significantly improve capacity, energy
Emerging memory technologies are promising
3D-Stacked DRAM | higher bandwidth | smaller capacity
Reduced-Latency DRAM (e.g., RL/TL-DRAM, FLY-RAM) | lower latency | higher cost
Low-Power DRAM (e.g., LPDDR3, LPDDR4, Voltron) | lower power | higher latency higher cost
Non-Volatile Memory (NVM) (e.g., PCM, STTRAM, ReRAM, 3D Xpoint) | larger capacity | higher latency higher dynamic power lower endurance

## Slide 22: Major Trend: Hybrid Main Memory
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 23: One Foreshadowing
Main Memory Needs
Intelligent Controllers

## Slide 24: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
Cross-Cutting Principles
Summary

## Slide 25: Three Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low Latency Architectures

## Slide 26: Maslow’s (Human) Hierarchy of Needs
We need to start with reliability and security…
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.

## Slide 27: How Reliable/Secure/Safe is This Bridge?
Source: http://www.technologystudent.com/struct1/tacom1.png

## Slide 28: Collapse of the “Galloping Gertie”
Source: AP

## Slide 29: How Secure Are These People?
Source: https://s-media-cache-ak0.pinimg.com/originals/48/09/54/4809543a9c7700246a0cf8acdae27abf.jpg
Security is about preventing unforeseen consequences

## Slide 30: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 31: As Memory Scales, It Becomes Unreliable
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 32: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 33: Infrastructures to Understand Such Issues
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 34: Infrastructures to Understand Such Issues
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 35: SoftMC: Open Source DRAM Infrastructure
Hasan Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 36: SoftMC
https://github.com/CMU-SAFARI/SoftMC

## Slide 37: Data Retention in Memory [Liu et al., ISCA 2013]
Retention Time Profile of DRAM looks like this:
Location dependent
Stored value pattern dependent
Time dependent
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 38: A Curious Discovery [Kim et al., ISCA 2014]
One can
predictably induce errors
in most DRAM memory chips

## Slide 39: DRAM RowHammer
A simple hardware failure mechanism
can create a widespread
system security vulnerability

## Slide 40: Modern DRAM is Prone to Disturbance Errors
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Hammered Row
Repeatedly reading a row enough times (before memory gets refreshed) induces disturbance errors in adjacent rows in most real DRAM chips you can buy today
Opened
Closed
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 41: Most DRAM Modules Are at Risk
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 42: Recent DRAM Is More Vulnerable
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 43: Recent DRAM Is More Vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 44: Recent DRAM Is More Vulnerable
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 45: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 46: A Simple Program Can Induce Many Errors
CPU
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Avoid cache hits
  Flush X from cache
Avoid row hits to X
  Read Y in another row
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 47: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 48: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 49: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 50: Observed Errors in Real Systems
A real reliability & security issue
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: When we executed the code on four different processors, all four of them yielded errors. Intel Haswell has the most errors, at 23 thousand, because it has the highest rate of accessing DRAM.
Later on, I’ll show that we can induce as many as ten million disturbance errors in a more controlled environment.
From this, we conclude that disturbance errors are a serious reliability issue.

## Slide 51: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn+, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)

## Slide 52: RowHammer Security Attack Example
“Rowhammer” is a problem with some recent DRAM devices in which repeatedly accessing a row of memory can cause bit flips in adjacent rows (Kim et al., ISCA 2014).
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
We tested a selection of laptops and found that a subset of them exhibited the problem.
We built two working privilege escalation exploits that use this effect.
  Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn+, 2015)
One exploit uses rowhammer-induced bit flips to gain kernel privileges on x86-64 Linux when run as an unprivileged userland process.
When run on a machine vulnerable to the rowhammer problem, the process was able to induce bit flips in page table entries (PTEs).
It was able to use this to gain write access to its own page table, and hence gain read-write access to all of physical memory.
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn & Dullien, 2015)

## Slide 53: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 54: More Security Implications
Source: https://lab.dsst.io/32c3-slides/7197.html
Rowhammer.js: A Remote Software-Induced Fault Attack in JavaScript (DIMVA’16)
“We can gain unrestricted access to systems of website visitors.”

## Slide 55: More Security Implications
Source: https://fossbytes.com/drammer-rowhammer-attack-android-root-devices/
Drammer: Deterministic Rowhammer Attacks on Mobile Platforms, CCS’16
  “Can gain control of a smart phone deterministically”

## Slide 56: More Security Implications?

## Slide 57: Apple’s Patch for RowHammer
https://support.apple.com/en-gb/HT204934
HP, Lenovo, and other vendors released similar patches

## Slide 58: Our Solution to RowHammer
PARA: Probabilistic Adjacent Row Activation
Key Idea
  After closing a row, we activate (i.e., refresh) one of its neighbors with a low probability: p = 0.005
Reliability Guarantee
  When p=0.005, errors in one year: 9.4×10-14
  By adjusting the value of p, we can vary the strength of protection against errors
Notes: We provide a more efficient solution, called PARA, which stands for probabilistic adjacent row activation.
The key idea is thus: after closing a row, we activate (i.e., refresh) one of its neighbors with a low probability, for example, p equal to 0.005.
PARA provides a strong reliability guarantee even under the worst-case access patterns to DRAM. When we set p to 0.005, the expected number of errors in one year is 9.4 times 10 to the negative 14. This probability is much lower the failure rate of other hardware components, for example, the hard-disk drive.
And by adjusting the value of p, PARA can provide an arbitrarily strong-degree of protection against errors.

## Slide 59: More on RowHammer Analysis
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data]

## Slide 60: Future of Memory Reliability
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 61: Industry Is Writing Papers About It, Too

## Slide 62: Call for Intelligent Memory Controllers

## Slide 63: Solution Direction: Principled Designs
Design fundamentally secure
computing architectures
Predict and prevent
such safety issues

## Slide 64: How Do We Keep Memory Secure?
Understand: Methodologies for failure modeling and discovery
  Modeling and prediction based on real (device) data
Architect: Principled co-architecting of system and memory
  Good partitioning of duties across the stack
Design & Test: Principled design, automation, testing
  High coverage and good interaction with system reliability methods

## Slide 65
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Understand and Model with Experiments (DRAM)

## Slide 66: Understand and Model with Experiments (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017, PIEEE’17]
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 67: Another Talk: NAND Flash Reliability
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" to appear in Proceedings of the IEEE, 2017.
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.
Fukami+, “Improving the Reliability of Chip-Off Forensic Analysis of NAND Flash Memory Devices,” DFRWS EU 2017.
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 68: NAND Flash Vulnerabilities
https://people.inf.ethz.ch/omutlu/pub/flash-memory-programming-vulnerabilities_hpca17.pdf
HPCA, Feb. 2017

## Slide 69: NAND Flash: Intelligent Memory Control
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 70: There are Two Other Solution Directions
New Technologies: Replace or (more likely) augment DRAM with a different technology
  Non-volatile memories
Embracing Un-reliability:
Design memories with different reliability
and store data intelligently across them
…
Fundamental solutions to security require co-design across the hierarchy
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 71: Exploiting Memory Error Tolerance with Hybrid Memory Systems
Chart: Memory error vulnerability
| App/Data A | App/Data B | App/Data C
System/Application Crash | 1.0414 | 0.63898 | 0.24773
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory [DSN 2014]
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search workload
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 72: More on Heterogeneous-Reliability Memory
Yixin Luo, Sriram Govindan, Bikash Sharma, Mark Santaniello, Justin Meza, Aman Kansal, Jie Liu, Badriddine Khessib, Kushagra Vaid, and Onur Mutlu, "Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost via Heterogeneous-Reliability Memory" Proceedings of the 44th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Atlanta, GA, June 2014. [Summary] [Slides (pptx) (pdf)] [Coverage on ZDNet]

## Slide 73: Summary: Memory Reliability and Security
Memory reliability is reducing
Reliability issues open up security vulnerabilities
  Very hard to defend against
Rowhammer is an example
  Its implications on system security research are tremendous & exciting
Good news: We have a lot more to do.
Understand: Solid methodologies for failure modeling and discovery
  Modeling based on real device data – small scale and large scale
Architect: Principled co-architecting of system and memory
  Good partitioning of duties across the stack
Design & Test: Principled electronic design, automation, testing
  High coverage and good interaction with system reliability methods

## Slide 74: Challenge and Opportunity for Future
Fundamentally
Secure, Reliable, Safe
Computing Architectures

## Slide 75: One Important Takeaway
Main Memory Needs
Intelligent Controllers

## Slide 76: Three Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low Latency Architectures

## Slide 77: Do We Want This?
Source: V. Milutinovic

## Slide 78: Or, This?
Source: V. Milutinovic

## Slide 79: Maslow’s (Human) Hierarchy of Needs, Revisited
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Everlasting energy
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.

## Slide 80: Challenge and Opportunity for Future
Sustainable
and
Energy Efficient

## Slide 81: Three Key Systems Trends
1. Data access is a major bottleneck
  Applications are increasingly data hungry
2. Energy consumption is a key limiter
3. Data movement energy dominates compute
  Especially true for off-chip to on-chip movement

## Slide 82: The Need for More Memory Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 83: The Performance Perspective (1996-2005)
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 84: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 85: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 86: The Performance Perspective
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors" Proceedings of the 9th International Symposium on High-Performance Computer Architecture (HPCA), pages 129-140, Anaheim, CA, February 2003. Slides (pdf)

## Slide 87: The Energy Perspective
Dally, HiPEAC 2015

## Slide 88: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 89: Data Movement vs. Computation Energy
Data movement is a major system energy bottleneck
  Comprises 41% of mobile system energy during web browsing [2]
  Costs ~115 times as much energy as an ADD operation [1, 2]
[1]: Reducing data Movement Energy via Online Data Clustering and Encoding (MICRO’16)
[2]: Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms (IISWC’14)

## Slide 90: Challenge and Opportunity for Future
High Performance
and
Energy Efficient

## Slide 91: The Problem
Data access is the major performance and energy bottleneck
Our current
design principles
cause great energy waste
(and great performance loss)

## Slide 92: The Problem
Processing of data
is performed
far away from the data

## Slide 93: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 94: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 95: Today’s Computing Systems
Are overwhelmingly processor centric
All data processed in the processor  at great system cost
Processor is heavily optimized and is considered the master
Data storage units are dumb and are largely unoptimized (except for some that are on the processor die)

## Slide 96: Yet …
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 97: Perils of Processor-Centric Design
Grossly-imbalanced systems
  Processing done only in one place
  Everything else just stores and moves data: data moves a lot
   Energy inefficient
   Low performance
   Complex
Overly complex and bloated processor (and accelerators)
  To tolerate data access from memory
  Complex hierarchies and mechanisms
   Energy inefficient
   Low performance
   Complex

## Slide 98: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data

## Slide 99: We Do Not Want to Move Data!
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition

## Slide 100: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 101: Goal: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processor chip?
  software and hardware interfaces?
  system software and languages?
  algorithms?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 102: Why In-Memory Computation Today?
Push from Technology
  DRAM Scaling at jeopardy
   Controllers close to DRAM
   Industry open to new memory architectures
Pull from Systems and Applications
  Data access is a major system and application bottleneck
  Systems are energy limited
  Data movement much more energy-hungry than computation
Dally, HiPEAC 2015

## Slide 103: Processing in Memory: Two Approaches
1. Minimally changing memory chips
2. Exploiting 3D-stacked memory

## Slide 104: Approach 1: Minimally Changing DRAM
DRAM has great capability to perform bulk data movement and computation internally with small changes
  Can exploit internal connectivity to move data
  Can exploit analog computation capability
  …
Examples: RowClone, In-DRAM AND/OR, Gather/Scatter DRAM
  RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data (Seshadri et al., MICRO 2013)
  Fast Bulk Bitwise AND and OR in DRAM (Seshadri et al., IEEE CAL 2015)
  Gather-Scatter DRAM: In-DRAM Address Translation to Improve the Spatial Locality of Non-unit Strided Accesses (Seshadri et al., MICRO 2015)
  "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology” (Seshadri et al., MICRO 2017)

## Slide 105: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 106: Today’s Systems: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 107: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 108: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 109: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 110: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 111: Memory as an Accelerator
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 112: In-Memory Bulk Bitwise Operations
We can support in-DRAM COPY, ZERO, AND, OR, NOT, MAJ
At low cost
Using analog computation capability of DRAM
  Idea: activating multiple rows performs computation
30-60X performance and energy improvement
  Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
New memory technologies enable even more opportunities
  Memristors, resistive RAM, phase change mem, STT-MRAM, …
  Can operate on data with minimal movement

## Slide 113: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 114: In-DRAM NOT: Dual Contact Cell
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
Idea:
Feed the
negated value
in the sense amplifier
into a special row

## Slide 115: Performance: In-DRAM Bitwise Operations

## Slide 116: Energy of In-DRAM Bitwise Operations
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 117: Ambit vs. DDR3: Performance and Energy
Chart: 
| not | and/or | nand/nor | xor/xnor | mean
Performance Improvement | 51.6251 | 38.3193 | 30.6965 | 21.8566 | 32
Energy Reduction | 59.5 | 43.9 | 35.1 | 25.1 | 35
32X
35X
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 118: Bulk Bitwise Operations in Workloads
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017

## Slide 119: Example Data Structure: Bitmap Index
Alternative to B-tree and its variants
Efficient for performing range queries and joins
Many bitwise operations to perform a query
Bitmap 1
Bitmap 2
Bitmap 4
Bitmap 3
age < 18
18 < age < 25
25 < age < 60
age > 60

## Slide 120: Performance: Bitmap Index on Ambit
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 121: Performance: BitWeaving on Ambit
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.

## Slide 122: More on In-DRAM Bulk AND/OR
Vivek Seshadri, Kevin Hsieh, Amirali Boroumand, Donghyuk Lee, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Fast Bulk Bitwise AND and OR in DRAM" IEEE Computer Architecture Letters (CAL), April 2015.

## Slide 123: More on Ambit
Vivek Seshadri et al., “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.

## Slide 124: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 125: Challenge: Intelligent Memory Device
Does memory
have to be
dumb?

## Slide 126: Processing in Memory: Two Approaches
1. Minimally changing memory chips
2. Exploiting 3D-stacked memory

## Slide 127: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 128: DRAM Landscape (circa 2015)
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.

## Slide 129: Two Key Questions in 3D-Stacked PIM
How can we accelerate important applications if we use 3D-stacked memory as a coarse-grained accelerator?
  what is the architecture and programming model?
  what are the mechanisms for acceleration?
What is the minimal processing-in-memory support we can provide?
  without changing the system significantly
  while achieving significant benefits

## Slide 130: Graph Processing
Large graphs are everywhere (circa 2015)
Scalable large-scale graph processing is challenging
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos
Chart: Speedup
| 128 Cores | 32 Cores
열3 | 1.4206 | 1

## Slide 131: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 132: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 133: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communications via Remote Function Calls

## Slide 134: Communications In Tesseract (I)

## Slide 135: Communications In Tesseract (II)

## Slide 136: Communications In Tesseract (III)

## Slide 137: Remote Function Call (Non-Blocking)

## Slide 138: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 139: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
Tesseract
32 Tesseract Cores
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 140: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
On five graph processing algorithms

## Slide 141: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
Chart: Memory Bandwidth Consumption
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 0.079545 | 0.1904 | 0.24289 | 1.2943 | 2.244 | 2.9197

## Slide 142: Effect of Bandwidth & Programming Model
Chart: Speedup
| HMC-MC | HMC-MC + PIM BW | Tesseract + Conventional BW | Tesseract
계열 1 | 1 | 2.3043 | 3.0224 | 6.4999
HMC-MC Bandwidth (640GB/s)
Tesseract Bandwidth (8TB/s)
Bandwidth
Programming Model
(No Prefetching)

## Slide 143: Tesseract Graph Processing System Energy
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
> 8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 144: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 145: Truly Distributed GPU Processing with PIM?
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
SM (Streaming Multiprocessor)

## Slide 146: Accelerating GPU Execution with PIM (I)
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 147: Accelerating GPU Execution with PIM (II)
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 148: Accelerating Linked Data Structures
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 149: Two Key Questions in 3D-Stacked PIM
How can we accelerate important applications if we use 3D-stacked memory as a coarse-grained accelerator?
  what is the architecture and programming model?
  what are the mechanisms for acceleration?
What is the minimal processing-in-memory support we can provide?
  without changing the system significantly
  while achieving significant benefits

## Slide 150: PIM-Enabled Instructions
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 151: Automatic Code and Data Mapping?
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 152: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 153: Challenge and Opportunity for Future
Fundamentally
Low-Latency
(Data-Centric)
Computing Architectures

## Slide 154: Three Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low Latency Architectures

## Slide 155
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 156: Maslow’s Hierarchy of Needs, A Third Time
Speed
Speed
Speed
Speed
Speed
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.

## Slide 157: See Backup Slides for Latency…

## Slide 158: Challenge and Opportunity for Future
Fundamentally
Low-Latency
Computing Architectures

## Slide 159: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
Cross-Cutting Principles
Summary

## Slide 160: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 161: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Data stored by changing phase of material
  Data read by detecting material’s resistance
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have (many) shortcomings
  Can they be enabled to replace/augment/surpass DRAM?
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 162: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 163: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 164: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 165: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 166: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 167: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 168: More on PCM As Main Memory
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)

## Slide 169: More on PCM As Main Memory (II)
Benjamin C. Lee, Ping Zhou, Jun Yang, Youtao Zhang, Bo Zhao, Engin Ipek, Onur Mutlu, and Doug Burger, "Phase Change Technology and the Future of Main Memory" IEEE Micro, Special Issue: Micro's Top Picks from 2009 Computer Architecture Conferences (MICRO TOP PICKS), Vol. 30, No. 1, pages 60-70, January/February 2010.

## Slide 170: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ) device
  Reference layer: Fixed magnetic orientation
  Free layer: Parallel or anti-parallel
Magnetic orientation of the free layer determines logical state of device
  High vs. low resistance
Write: Push large current through MTJ to change orientation of free layer
Read: Sense current flow
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 171: STT-MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatile  Persistent
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Poor density (currently)
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 172: Architected STT-MRAM as Main Memory
4-core, 4GB main memory, multiprogrammed workloads
~6% performance loss, ~60% energy savings vs. DRAM
Chart: Performance vs. DRAM
STT-RAM (base) | 0.95574 | 0.91812 | 0.93435 | 0.95579 | 0.95738 | 0.92083 | 0.95404 | 0.93019 | 0.95413 | 0.94507 | 0.92103 | 0.94061
STT-RAM (opt) | 0.96014 | 0.91453 | 0.9443 | 0.95632 | 0.95951 | 0.92092 | 0.95948 | 0.93564 | 0.96003 | 0.94574 | 0.93546 | 0.94473
Chart: Energy vs. DRAM
| mpmix0 | mpmix1 | mpmix2 | mpmix3 | mpmix4 | mpmix5 | mpmix6 | mpmix7 | mpmix8 | mpmix9 | mpmix10 | Average
ACT+PRE | 0.30175 | 0.27646 | 0.37425 | 0.32119 | 0.33973 | 0.34883 | 0.36197 | 0.2603 | 0.33524 | 0.39385 | 0.32655 | 0.33092
WB | 0.018529 | 0.027397 | 0.013518 | 0.015979 | 0.022233 | 0.018649 | 0.015872 | 0.025826 | 0.01687 | 0.016362 | 0.015008 | 0.018749
RB | 0.01752 | 0.014162 | 0.010281 | 0.018781 | 0.023665 | 0.010148 | 0.024161 | 0.016986 | 0.013315 | 0.012743 | 0.010166 | 0.01563
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 173: More on STT-MRAM as Main Memory
Emre Kultursay, Mahmut Kandemir, Anand Sivasubramaniam, and Onur Mutlu, "Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative" Proceedings of the 2013 IEEE International Symposium on Performance Analysis of Systems and Software (ISPASS), Austin, TX, April 2013. Slides (pptx) (pdf)

## Slide 174: A More Viable Approach: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAM Ctrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 175: A More Viable Approach: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 176: Challenge and Opportunity
Providing the Best of
Multiple Metrics
with
Multiple Memory Technologies

## Slide 177: Challenge and Opportunity
Heterogeneous,
Configurable,
Programmable
Memory Systems

## Slide 178: Hybrid Memory Systems: Issues
Cache vs. Main Memory
Granularity of Data Move/Manage-ment: Fine or Coarse
Hardware vs. Software vs. HW/SW Cooperative
When to migrate data?
How to design a scalable and efficient large cache?
…

## Slide 179: On Hybrid Memory Data Placement (I)
HanBin Yoon, Justin Meza, Rachata Ausavarungnirun, Rachael Harding, and Onur Mutlu, "Row Buffer Locality Aware Caching Policies for Hybrid Memories" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (pptx) (pdf)

## Slide 180: On Hybrid Memory Data Placement (II)
Yang Li, Saugata Ghose, Jongmoo Choi, Jin Sun, Hui Wang, and Onur Mutlu, "Utility-Based Hybrid Memory Management" Proceedings of the 19th IEEE Cluster Conference (CLUSTER), Honolulu, Hawaii, USA, September 2017. [Slides (pptx) (pdf)]

## Slide 181: On Large DRAM Cache Design (I)
Justin Meza, Jichuan Chang, HanBin Yoon, Onur Mutlu, and Parthasarathy Ranganathan, "Enabling Efficient and Scalable Hybrid Memories Using Fine-Granularity DRAM Cache Management" IEEE Computer Architecture Letters (CAL), February 2012.

## Slide 182: On Large DRAM Cache Design (II)
Xiangyao Yu, Christopher J. Hughes, Nadathur Satish, Onur Mutlu, and Srinivas Devadas, "Banshee: Bandwidth-Efficient DRAM Caching via Software/Hardware Cooperation" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017.

## Slide 183: Challenge and Opportunity
Enabling
an Emerging Technology
to Augment DRAM
Managing Hybrid Memories

## Slide 184: Other Opportunities with Emerging Technologies
Merging of memory and storage
  e.g., a single interface to manage all data
New applications
  e.g., ultra-fast checkpoint and restore
More robust system design
  e.g., reducing data loss
Processing tightly-coupled with memory
  e.g., enabling efficient search and filtering

## Slide 185: TWO-LEVEL STORAGE MODEL
CPU
MEMORY
STORAGE
VOLATILE
FAST
BYTE ADDR
NONVOLATILE
SLOW
BLOCK ADDR
Ld/St
FILE
I/O
DRAM
Notes: If we look at our system’s today, we have a two-level storage model where memory is directly accessed by ld/st instructions, but storage is accesses by system calls. Disk stores the persistent data, but is slow and can only be accessed as a block. So we transfer data to DRAM, which is fast and byte addressable.

## Slide 186: TWO-LEVEL STORAGE MODEL
CPU
MEMORY
STORAGE
VOLATILE
FAST
BYTE ADDR
NONVOLATILE
SLOW
BLOCK ADDR
Ld/St
FILE
I/O
DRAM
PCM, STT-RAM
NVM
Non-volatile memories combine characteristics of memory and storage
Notes: However, now we have these emerging non-volatile memories which actually combine the characteristics of both memory and storage. They are fast and byte addressable like DRAM, but also can persist data as storage

## Slide 187: Two-Level Memory/Storage Model
The traditional two-level storage model is a bottleneck with NVM
  Volatile data in memory  a load/store interface
  Persistent data in storage  a file system interface
  Problem: Operating system (OS) and file system (FS) code to locate, translate, buffer data become performance and energy bottlenecks with fast NVM stores
Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …
Persistent (e.g., Phase-Change)
Memory

## Slide 188: Unified Memory and Storage with NVM
Goal: Unify memory and storage management in a single unit to eliminate wasted work to locate, transfer, and translate data
  Improves both energy and performance
  Simplifies programming model as well
Unified Memory/Storage
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 189: The Persistent Memory Manager (PMM)
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Persistent objects
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 190: Performance Benefits of a Single-Level Store
~5X
~24X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 191: Energy Benefits of a Single-Level Store
~5X
~16X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 192: On Persistent Memory Benefits & Challenges
Justin Meza, Yixin Luo, Samira Khan, Jishen Zhao, Yuan Xie, and Onur Mutlu, "A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory" Proceedings of the 5th Workshop on Energy-Efficient Design (WEED), Tel-Aviv, Israel, June 2013. Slides (pptx) Slides (pdf)

## Slide 193: Challenge and Opportunity
Combined
Memory & Storage

## Slide 194: Challenge and Opportunity
A Unified Interface to All Data

## Slide 195: Another Key Challenge in Persistent Memory
Programming Ease
to Exploit Persistence

## Slide 196: Hardware Support for Crash Consistency
Jinglei Ren, Jishen Zhao, Samira Khan, Jongmoo Choi, Yongwei Wu, and Onur Mutlu, "ThyNVM: Enabling Software-Transparent Crash Consistency in Persistent Memory Systems" Proceedings of the 48th International Symposium on Microarchitecture (MICRO), Waikiki, Hawaii, USA, December 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Source Code]

## Slide 197: Tools/Libraries to Help Programmers
Himanshu Chauhan, Irina Calciu, Vijay Chidambaram, Eric Schkufza, Onur Mutlu, and Pratap Subrahmanyam, "NVMove: Helping Programmers Move to Byte-Based Persistence" Proceedings of the 4th Workshop on Interactions of NVM/Flash with Operating Systems and Workloads (INFLOW), Savannah, GA, USA, November 2016. [Slides (pptx) (pdf)]

## Slide 198: Data Structures for In-Memory Processing
Zhiyu Liu, Irina Calciu, Maurice Herlihy, and Onur Mutlu, "Concurrent Data Structures for Near-Memory Computing" Proceedings of the 29th ACM Symposium on Parallelism in Algorithms and Architectures (SPAA), Washington, DC, USA, July 2017. [Slides (pptx) (pdf)]

## Slide 199: Concluding Remarks

## Slide 200: A Quote from A Famous Architect
“architecture […] based upon principle, and not upon precedent”

## Slide 201: Precedent-Based Design?
“architecture […] based upon principle, and not upon precedent”

## Slide 202: Principled Design
“architecture […] based upon principle, and not upon precedent”

## Slide 204: The Overarching Principle

## Slide 205: Another Example: Precedent-Based Design
Source: http://cookiemagik.deviantart.com/art/Train-station-207266944

## Slide 206: Principled Design
Source: By Toni_V, CC BY-SA 2.0, https://commons.wikimedia.org/w/index.php?curid=4087256

## Slide 207: Another Principled Design
Source: By Martín Gómez Tagle - Lisbon, Portugal, CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=13764903
Source: http://www.arcspace.com/exhibitions/unsorted/santiago-calatrava/

## Slide 208: Principle Applied to Another Structure
Source: https://www.dezeen.com/2016/08/29/santiago-calatrava-oculus-world-trade-center-transportation-hub-new-york-photographs-hufton-crow/
Source: By 準建築人手札網站 Forgemind ArchiMedia - Flickr: IMG_2489.JPG, CC BY 2.0,
https://commons.wikimedia.org/w/index.php?curid=31493356, https://en.wikipedia.org/wiki/Santiago_Calatrava

## Slide 209: The Overarching Principle

## Slide 210: Overarching Principles for Computing?
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 211: Concluding Remarks
It is time to design principled system architectures to solve the memory scaling problem
Discover design principles for fundamentally secure and reliable computer architectures
Design complete systems to be balanced and energy-efficient, i.e., data-centric (or memory-centric) and low latency
Enable new and emerging memory architectures
This can
  Lead to orders-of-magnitude improvements
  Enable new applications & computing platforms
  …
Notes: Perhaps we have taken processor-centric system design a bit too far

## Slide 212: The Future of New Memory is Bright
Regardless of challenges
  in underlying technology and overlying problems/requirements
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Can enable:
- Orders of magnitude
improvements
- New applications and
computing systems
Yet, we have to
- Think across the stack
- Design enabling systems

## Slide 213: If In Doubt, See Other Doubtful Technologies
A very “doubtful” emerging technology
  for at least two decades
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 214: Rethinking Memory System Design (and the Platforms We Design Around It)
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
December 4, 2017
INESC-ID Distinguished Lecture (Lisbon)

## Slide 215: Open Problems

## Slide 216: For More Open Problems, See (I)
Onur Mutlu and Lavanya Subramanian, "Research Problems and Opportunities in Memory Systems" Invited Article in Supercomputing Frontiers and Innovations (SUPERFRI), 2014/2015.
https://people.inf.ethz.ch/omutlu/pub/memory-systems-research_superfri14.pdf

## Slide 217: For More Open Problems, See (II)
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 218: For More Open Problems, See (III)
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Technical talk at MemCon 2013 (MEMCON), Santa Clara, CA, August 2013. [Slides (pptx) (pdf)] [Video] [Coverage on StorageSearch]
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 219: For More Open Problems, See (IV)
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" to appear in Proceedings of the IEEE, 2017. [Preliminary arxiv.org version]
https://arxiv.org/pdf/1706.08642.pdf

## Slide 220: Reducing Memory Latency

## Slide 221: Main Memory Latency Lags Behind
Chart: DRAM Improvement (log)
| 1999.0 | 2003.0 | 2006.0 | 2008.0 | 2011.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 222: A Closer Look …
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 223: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 224: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 225: Why the Long Latency?
Design of DRAM uArchitecture
  Goal: Maximize capacity/area, not minimize latency
“One size fits all” approach to latency specification
  Same latency parameters for all temperatures
  Same latency parameters for all DRAM chips (e.g., rows)
  Same latency parameters for all parts of a DRAM chip
  Same latency parameters for all supply voltage levels
  Same latency parameters for all application data
  …

## Slide 226: Latency Variation in Memory Chips
High
Low
DRAM Latency
DRAM B
DRAM A
DRAM C
Slow cells
Heterogeneous manufacturing & operating conditions → latency variation in timing parameters

## Slide 227: DRAM Characterization Infrastructure
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 228: DRAM Characterization Infrastructure
Hasan Hassan et al., SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies, HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 229: SoftMC: Open Source DRAM Infrastructure
https://github.com/CMU-SAFARI/SoftMC

## Slide 230: Tackling the Fixed Latency Mindset
Reliable operation latency is actually very heterogeneous
  Across temperatures, chips, parts of a chip, voltage levels, …
Idea: Dynamically find out and use the lowest latency one can reliably access a memory location with
  Adaptive-Latency DRAM [HPCA 2015]
  Flexible-Latency DRAM [SIGMETRICS 2016]
  Design-Induced Variation-Aware DRAM [SIGMETRICS 2017]
  Voltron [SIGMETRICS 2017]
  ...
We would like to find sources of latency heterogeneity and exploit them to minimize latency

## Slide 231: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer provides multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 232
Latency Reduction Summary of 115 DIMMs
Latency reduction for read & write (55°C)
  Read Latency: 32.7%
  Write Latency: 55.1%
Latency reduction for each timing parameter (55°C)
  Sensing: 17.3%
  Restore: 37.3% (read), 54.8% (write)
  Precharge: 35.2%
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 233
AL-DRAM: Real System Evaluation
System
  CPU: AMD 4386 ( 8 Cores, 3.1GHz, 8MB LLC)
  DRAM: 4GByte DDR3-1600 (800Mhz Clock)
  OS: Linux
  Storage: 128GByte SSD
Workload
  35 applications from SPEC, STREAM, Parsec, Memcached, Apache, GUPS

## Slide 234
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
1.4%
6.7%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
5.0%
AL-DRAM: Single-Core Evaluation
AL-DRAM improves single-core performance
on a real system
Performance Improvement
Average
Improvement
all-35-workload

## Slide 235
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
AL-DRAM: Multi-Core Evaluation
AL-DRAM provides higher performance on
multi-programmed & multi-threaded workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 236: Reducing Latency Also Reduces Energy
AL-DRAM reduces DRAM power consumption by 5.8%
Major reason: reduction in row activation time

## Slide 237: More on Adaptive-Latency DRAM
Donghyuk Lee, Yoongu Kim, Gennady Pekhimenko, Samira Khan, Vivek Seshadri, Kevin Chang, and Onur Mutlu, "Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)] [Full data sets]

## Slide 238: Heterogeneous Latency within A Chip
Chart: 40 Workloads
Baseline (DDR3) | 1
FLY-DRAM (D1) | 1.133
FLY-DRAM (D2) | 1.176
FLY-DRAM (D3) | 1.195
Upper Bound | 1.197
17.6%
19.5%
19.7%
13.3%
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 239: Analysis of Latency Variation in DRAM Chips
Kevin Chang, Abhijith Kashyap, Hasan Hassan, Samira Khan, Kevin Hsieh, Donghyuk Lee, Saugata Ghose, Gennady Pekhimenko, Tianshi Li, and Onur Mutlu, "Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Antibes Juan-Les-Pins, France, June 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 240
Inherently fast
inherently slow
What Is Design-Induced Variation?
slow
fast
slow
fast
Systematic variation in cell access times
caused by the physical organization of DRAM
sense amplifiers
wordline drivers
across row
distance from sense amplifier
across column
distance from wordline driver
Notes: As we described, cells in a mat have different distances from peripheral logic.
Cells in different rows have different distance from the sense amplifiers.
Cells in different columns have different distance from the wordline drivers.
Therefore, some regions are inherently faster than other regions,
and some regions are inherently slower than other regions.
We call this architectural variation.

## Slide 241
DIVA Online Profiling
inherently slow
Profile only slow regions to determine min. latency
 Dynamic & low cost latency optimization
sense amplifier
wordline driver
Design-Induced-Variation-Aware
Notes: We propoe AVA Online profiling.
The key idea is profiling only slow regions to determine latency, leading to low cost online DRAM test.

## Slide 242
inherently slow
DIVA Online Profiling
slow cells
design-induced
variation
process
variation
localized error
random error
online profiling
error-correcting code
Combine error-correcting codes & online profiling
 Reliably reduce DRAM latency
sense amplifier
wordline driver
Design-Induced-Variation-Aware
Notes: However, due to the process variation, some cells are more vulnerable than other cells, as the figure show.
These cells are randomly distributed while cells in the slow regions cause localized error.
To address both type of cells,
We integrate conventional ECC to correct the process variation induced errors.
Therefore, combining ECC and online profiling leads to reliably reducing DRAM latency.

## Slide 243
DIVA-DRAM Reduces Latency
Read
Write
Chart: 
| 55°C | 85°C | 55°C | 85°C | 55°C | 85°C | AL-DRAM | AVA Profiling | AVA Profiling + Shuffling
Latency Reduction | 0.31202 | 0.25527 | 0.35118 | 0.3464 | 0.36569 | 0.358
Latency Reduction
DIVA
DIVA
Chart: 
| 55°C | 85°C | 55°C | 85°C | 55°C | 85°C | AL-DRAM | AVA Profiling | AVA Profiling + Shuffling
Latency Reduction | 0.36561 | 0.27539 | 0.394 | 0.38718 | 0.41294 | 0.40274
DIVA
DIVA
DIVA-DRAM reduces latency more aggressively and uses ECC to correct random slow cells
Notes: The figure compares latency reduction by using AL-DRAM, AVA Profiling, and both AVA Profiling and Shuffling.
As we can, using AVA profiling and shuffling enables more latency reduction compared to AL-DRAM.
This is mainly because ECC corrects the worst cells in a DRAM module, reducing more latency.
Therefore, we conclude that AVA-DRAM reduces latency significantly.

## Slide 244: Design-Induced Latency Variation in DRAM
Donghyuk Lee, Samira Khan, Lavanya Subramanian, Saugata Ghose, Rachata Ausavarungnirun, Gennady Pekhimenko, Vivek Seshadri, and Onur Mutlu, "Design-Induced Latency Variation in Modern DRAM Chips: Characterization, Analysis, and Latency Reduction Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 245: Voltron: Exploiting the Voltage-Latency-Reliability Relationship

## Slide 246: Executive Summary
DRAM (memory) power is significant in today’s systems
  Existing low-voltage DRAM reduces voltage conservatively
Goal: Understand and exploit the reliability and latency behavior of real DRAM chips under aggressive reduced-voltage operation
Key experimental observations:
  Huge voltage margin -- Errors occur beyond some voltage
  Errors exhibit spatial locality
  Higher operation latency mitigates voltage-induced errors
Voltron: A new DRAM energy reduction mechanism
  Reduce DRAM voltage without introducing errors
  Use a regression model to select voltage that does not degrade performance beyond a chosen target  7.3% system energy reduction

## Slide 247: Analysis of Latency-Voltage in DRAM Chips
Kevin Chang, A. Giray Yaglikci, Saugata Ghose, Aditya Agrawal, Niladrish Chatterjee, Abhijith Kashyap, Donghyuk Lee, Mike O'Connor, Hasan Hassan, and Onur Mutlu, "Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 248: And, What If …
… we can sacrifice reliability of some data to access it with even lower latency?

## Slide 249: Challenge and Opportunity for Future
Fundamentally
Low Latency
Computing Architectures

## Slide 250: Tiered Latency DRAM

## Slide 251: What Causes the Long Latency?
DRAM Latency = Subarray Latency + I/O Latency
DRAM Chip
channel
cell array
I/O
DRAM Chip
channel
I/O
subarray
DRAM Latency = Subarray Latency + I/O Latency
Dominant
Subarray
I/O
Notes: To understand what causes the long latency, let me take a look at the DRAM organization.
DRAM consists of two components, the cell array and the I/O circuitry. The cell array consists of multiple subarrays.
To read from a DRAM chip, the data is first accessed from the subarray and then the data is transferred over the channel by the I/O circuitry.
So, the DRAM latency is the sum of the subarray latency and the I/O latency.
We observed that the subarray latency is much higher than the I/O latency.
As a result, subarray is the dominant source of the DRAM latency as we explained in the paper.

## Slide 252: Why is the Subarray So Slow?
Subarray
row decoder
sense amplifier
capacitor
access
transistor
wordline
bitline
Cell
large sense amplifier
bitline: 512 cells
cell
Long bitline
  Amortizes sense amplifier cost  Small area
  Large bitline capacitance  High latency & power
sense amplifier
row decoder
Notes: The cell’s capacitor is small and can store only a small amount of charge.
That is why a subarray also has sense-amplifiers, which are specialized circuits that can detect the small amount of charge.
Unfortunately, a sense-amplifier size is about *100* times the cell size.
So, to amortize the area of the sense-amplifiers,
hundreds of cells share the same sense-amplifier through a long bitline.
However, a long bitline has a large capacitance that increases latency and power consumption.
Therefore, the long bitline is one of the dominant sources of high latency and high power consumption.
To understand why the subarray is so slow,
let me take a look at the subarray organization.

## Slide 253: Trade-Off: Area (Die Size) vs. Latency
Faster
Smaller
Short Bitline
Long Bitline
Trade-Off: Area vs. Latency
Notes: A naïve way to reduce the DRAM latency is to have short bitlines that have lower latency.
Unfortunately, short bitlines significantly increase the DRAM area.
Therefore, the bitline length exposes an important trade-off between area and latency.

## Slide 254: Trade-Off: Area (Die Size) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.61776435004466 | 27.83117556055124 | 35.46159936378587 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Commodity DRAM
Long Bitline
Cheaper
Faster
Fancy DRAM
Short Bitline
GOAL
Notes: This figure shows the trade-off between DRAM area and latency as we change the bitline length.
Y-axis is the normalized DRAM area compared to a DRAM using 512 cells/bitline. A lower value is cheaper.
X-axis shows the latency in terms of tRC, an important DRAM timing constraint. A lower value is faster.
Commodity DRAM chips use long bitlines to minimize area cost. On the other hand, shorter bitlines achieve lower latency at higher cost.
Our goal is to achieve the best of both worlds: low latency and low area cost.

## Slide 255: Approximating the Best of Both Worlds
Short Bitline
Low Latency
Long Bitline
Small Area
Long Bitline
Low Latency
Short Bitline
Our Proposal
Small Area
Short Bitline  Fast
Need Isolation
Add Isolation Transistors
High Latency
Large Area
Notes: To sum up, both long and short bitline do not achieve small area and low latency.
Long bitline has small area but has high latency while short bitline has low latency but has large area.
To achieve the best of both worlds, we first start from long bitline, which has small area.
After that, to achieve the low latency of short bitline, we divide the long bitline into two smaller segments.
The bitline length of the segment nearby the sense-amplifier is same as the length of short bitline.
Therefore, the latency of the segment is as low as the latency of the short bitline.
To isolate this fast segment from the other segment, we add isolation transistors that selectively connect the two segments.

## Slide 256: Approximating the Best of Both Worlds
Low Latency
Our Proposal
Small Area
Long Bitline
Small Area
Long Bitline
High Latency
Short Bitline
Low Latency
Short Bitline
Large Area
Tiered-Latency DRAM
Low Latency
Small area using long bitline
Notes: This way, our proposed approach achieves small area and low latency.
We call this new DRAM architecture as Tiered-Latency DRAM

## Slide 257: Commodity DRAM vs. TL-DRAM [HPCA 2013]
Chart: 
| commodity DRAM | near segment | far segment
Normalized Power Consumption | 1 | 0.49 | 1.49
Chart: 
| commodity DRAM | near segment | far segment
Latency | 1 | 0.56 | 1.23
Latency
Power
  –56%
  +23%
  –51%
  +49%
DRAM Latency (tRC)
DRAM Power
DRAM Area Overhead
  ~3%: mainly due to the isolation transistors
  TL-DRAM
  Commodity DRAM
  Near Far
  Commodity DRAM
  Near Far
  TL-DRAM
  (52.5ns)
Notes: This figure compares the latency.
Y-axis is normalized latency.
Compared to commodity DRAM, TL-DRAM’s near segment has 56% lower latency, while the far segment has 23% higher latency.
The right figure compares the power.
Y-axis is normalized power.
Compared to commodity DRAM, TL-DRAM’s near segment has 51% lower power consumption and the far segment has 49% higher power consumption.
Lastly, mainly due to the isolation transistor, Tiered-latency DRAM increases the die-size by about 3%.

## Slide 258: Trade-Off: Area (Die-Area) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.61776435004466 | 27.83117556055124 | 35.46159936378587 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Cheaper
Faster
Near Segment
Far Segment
GOAL
Notes: Again, the figure shows the trade-off between area and latency in existing DRAM.
Unlike existing DRAM, TL-DRAM achieves low latency using the near segment while increasing the area by only 3%.
Although the far segment has higher latency than commodity DRAM, we show that efficient use of the near segment enables TL-DRAM to achieve high system performance.

## Slide 259: Leveraging Tiered-Latency DRAM
TL-DRAM is a substrate that can be leveraged by the hardware and/or software
Many potential uses
  Use near segment as hardware-managed inclusive cache to far segment
  Use near segment as hardware-managed exclusive cache to far segment
  Profile-based page mapping by operating system
  Simply replace DRAM with TL-DRAM
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: There are multiple ways to leverage the TL-DRAM substrate by hardware or software.
In this slide, I describe many such ways.
First, the near segment can be used as a hardware-managed inclusive cache to the far segment.
Second, the near segment can be used as a hardware-managed exclusive cache to the far segment.
Third, the operating system can intelligently allocate frequently-accessed pages to the near segment.
Forth mechanism is to simple replace DRAM with TL-DRAM without any near segment handling
While our paper provides detailed explanations and evaluations of first three mechanism,
in this talk, we will focus on the first approach, which is to use the near segment as a hardware managed cache for the far segment.

## Slide 260: Performance & Power Consumption
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Performance Improvement | 1.124 | 1.115 | 1.107
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Power Reduction | 0.769 | 0.755 | 0.737
11.5%
Normalized Performance
Core-Count (Channel)
Normalized Power
Core-Count (Channel)
10.7%
12.4%
–23%
–24%
–26%
Using near segment as a cache improves performance and reduces power consumption
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: This figure shows the IPC improvement of our three caching mechanisms over commodity DRAM.
All of them improve performance and benefit-based caching shows maximum performance improvement by 12.7%.
The right figure shows the normalized power reduction of our three caching mechanisms over commodity DRAM.
All of them reduce power consumption and benefit-based caching shows maximum power reduction by 23%.
Therefore, using near segment as a cache improves performance and reduces power consumption at the cost of 3% area overhead.

## Slide 261: More on PIM

## Slide 262: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 263: Barriers to Adoption of PIM
1. Functionality of and applications for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System support: coherence & virtual memory
4. Runtime systems for adaptive scheduling, data mapping, access/sharing control
5. Infrastructures to assess benefits and feasibility

## Slide 264: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 265: Key Challenge 1: Code Mapping
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
?
Main GPU
3D-stacked memory
(memory stack)
Challenge 1: Which operations should be executed in memory vs. in CPU?
?
SM (Streaming Multiprocessor)

## Slide 266: Key Challenge 2: Data Mapping
Logic layer SM
Crossbar switch
Vault Ctrl
….
Vault Ctrl
Logic layer
Main GPU
3D-stacked memory
(memory stack)
Challenge 2: How should data be mapped to different 3D memory stacks?
SM (Streaming Multiprocessor)

## Slide 267: How to Do the Code and Data Mapping?
Kevin Hsieh, Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee, Mike O'Connor, Nandita Vijaykumar, Onur Mutlu, and Stephen W. Keckler, "Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems" Proceedings of the 43rd International Symposium on Computer Architecture (ISCA), Seoul, South Korea, June 2016. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 268: How to Schedule Code?
Ashutosh Pattnaik, Xulong Tang, Adwait Jog, Onur Kayiran, Asit K. Mishra, Mahmut T. Kandemir, Onur Mutlu, and Chita R. Das, "Scheduling Techniques for GPU Architectures with Processing-In-Memory Capabilities" Proceedings of the 25th International Conference on Parallel Architectures and Compilation Techniques (PACT), Haifa, Israel, September 2016.

## Slide 269: Challenge: Coherence for Hybrid CPU-PIM Apps
Traditional
coherence
No coherence
overhead

## Slide 270: How to Maintain Coherence?
Amirali Boroumand, Saugata Ghose, Minesh Patel, Hasan Hassan, Brandon Lucia, Kevin Hsieh, Krishna T. Malladi, Hongzhong Zheng, and Onur Mutlu, "LazyPIM: An Efficient Cache Coherence Mechanism for Processing-in-Memory" IEEE Computer Architecture Letters (CAL), June 2016.

## Slide 271: How to Support Virtual Memory?
Kevin Hsieh, Samira Khan, Nandita Vijaykumar, Kevin K. Chang, Amirali Boroumand, Saugata Ghose, and Onur Mutlu, "Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation" Proceedings of the 34th IEEE International Conference on Computer Design (ICCD), Phoenix, AZ, USA, October 2016.

## Slide 272: How to Design Data Structures for PIM?
Zhiyu Liu, Irina Calciu, Maurice Herlihy, and Onur Mutlu, "Concurrent Data Structures for Near-Memory Computing" Proceedings of the 29th ACM Symposium on Parallelism in Algorithms and Architectures (SPAA), Washington, DC, USA, July 2017. [Slides (pptx) (pdf)]

## Slide 273: Simulation Infrastructures for PIM
Ramulator extended for PIM
  Flexible and extensible DRAM simulator
  Can model many different memory standards and proposals
  Kim+, “Ramulator: A Flexible and Extensible DRAM Simulator”, IEEE CAL 2015.
  https://github.com/CMU-SAFARI/ramulator

## Slide 274: An FPGA-based Test-bed for PIM?
Hasan Hassan et al., SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 275: Some PIM Applications

## Slide 276: Goals
Understand the primitives, architectures, and benefits of PIM by carefully examining many important workloads
Develop a common workload suite for PIM research

## Slide 277: Genome Read In-Memory (GRIM) Filter: Fast Location Filtering in DNA Read Mapping with Emerging Memory Technologies
Jeremie Kim,
Damla Senol, Hongyi Xin, Donghyuk Lee,
Saugata Ghose, Mohammed Alser, Hasan Hassan,
Oguz Ergin, Can Alkan, and Onur Mutlu
Notes: Hello, my name is Jeremie Kim and I will be presenting Genome Read In-Memory Filter which will also be referred to as GRIM-Filter for short.
[CLICK]

## Slide 278: Executive Summary
Genome Read Mapping is a very important problem and is the first step in many types of genomic analysis
  Could lead to improved health care, medicine, quality of life
Read mapping is an approximate string matching problem
  Find the best fit of 100 character strings into a 3 billion character dictionary
  Alignment is currently the best method for determining the similarity between two strings, but is very expensive
We propose an in-memory processing algorithm GRIM-Filter for accelerating read mapping, by reducing the number of required alignments
We implement GRIM-Filter using in-memory processing within 3D-stacked memory and show up to 3.7x speedup.

## Slide 279: GRIM-Filter in 3D-stacked DRAM
The layout of bit vectors in a bank enables filtering many bins in parallel
Customized logic for accumulation and comparison per genome segment
  Low area overhead, simple implementation
Notes: [CLICK]
Each DRAM layer is organized as an array of Banks
[CLICK]
and a bank is an array of cells with a row buffer. The row buffer holds one row at a time and uses this structure to transfer data with high bandwidth into the logic layer via TSVs
[CLICK]
We now show the distribution of bit vectors across the DRAM arrays to enable parallel processing of many bins.
[CLICK]
Each row represents a token's occurrence across many sequential bins. and the row of the appropriate token gets queried to find a vector showing the occurrence of the token across many bins.
These are the vectors are brought down into the logic layer to be operated on.
[CLICK]
[END-CLICK]

## Slide 280: GRIM-Filter Performance
Time (x1000 seconds)
1.8x-3.7x performance benefit across real data sets
Benchmarks and their Execution Times
Notes: We ran 10 separate experiments with real read data sets, consisting of approximately 4 million reads each, and got the following results. Compared to the previous best filter, our filter enjoys a 2x average end-to-end read mapper performance gain across the data sets, and a 6x average lower false positive rate. Again, these are the locations that were not discarded by the filter, but were then later discarded after alignment

## Slide 281: GRIM-Filter False Positive Rate
False Positive Rate (%)
5.6x-6.4x False Positive reduction across real data sets
Benchmarks and their False Positive Rates
Notes: We ran 10 separate experiments with real read data sets, consisting of approximately 4 million reads each, and got the following results. Compared to the previous best filter, our filter enjoys a 2x average end-to-end read mapper performance gain across the data sets, and a 6x average lower false positive rate. Again, these are the locations that were not discarded by the filter, but were then later discarded after alignment

## Slide 282: Conclusions
We propose an in memory filter algorithm to accelerate end-to-end genome read mapping by reducing the number of required alignments
Compared to the previous best filter
  We observed 1.8x-3.7x speedup
  We observed 5.6x-6.4x fewer false positives
GRIM-Filter is a universal filter that can be applied to any genome read mapper
Notes: [CLICK]
We propose an in-memory filter to accelerate read mapping
[CLICK]
Compared to the previous best filter we show up to 3.7x end-to-end speedup on the same mapper and
We also observe on average 6x fewer false positives
[CLICK]
GRIM-Filter is a universal filter that can be applied to any read mapper and we hope these results encourage people to use processing in memory to improve other data intensive algorithms
[END-CLICK]

## Slide 283: PIM-Based DNA Sequence Analysis
Jeremie Kim, Damla Senol, Hongyi Xin, Donghyuk Lee, Mohammed Alser, Hasan Hassan, Oguz Ergin, Can Alkan, and Onur Mutlu, "Genome Read In-Memory (GRIM) Filter: Fast Location Filtering in DNA Read Mapping Using Emerging Memory Technologies" Pacific Symposium on Biocomputing (PSB) Poster Session, Hawaii, January 2017. [Poster (pdf) (pptx)] [Abstract (pdf)]
To Appear in APBC 2018 and BMC Genomics 2018.

## Slide 284: PIM-Enabled Instructions

## Slide 285: PEI: PIM-Enabled Instructions (Ideas)
Goal: Develop mechanisms to get the most out of near-data processing with minimal cost, minimal changes to the system, no changes to the programming model
Key Idea 1: Expose each PIM operation as a cache-coherent, virtually-addressed host processor instruction (called PEI) that operates on only a single cache block
  e.g., __pim_add(&w.next_rank, value)  pim.add r1, (r2)
  No changes sequential execution/programming model
  No changes to virtual memory
  Minimal changes to cache coherence
  No need for data mapping: Each PEI restricted to a single memory module
Key Idea 2: Dynamically decide where to execute a PEI (i.e., the host processor or PIM accelerator) based on simple locality characteristics and simple hardware predictors
  Execute each operation at the location that provides the best performance

## Slide 286: Simple PIM Operations as ISA Extensions (I)
Main Memory
w.next_rank
w.next_rank
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}
Host Processor
w.next_rank
w.next_rank
64 bytes in
64 bytes out
Conventional Architecture

## Slide 287: Simple PIM Operations as ISA Extensions (II)
Main Memory
w.next_rank
w.next_rank
Host Processor
value
8 bytes in
0 bytes out
In-Memory Addition
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pim.add r1, (r2)

## Slide 288: Always Executing in Memory? Not A Good Idea
Chart: Speedup
| p2p-Gnu tella31 | soc-Slash dot0811 | web- Stanford | amazon- 2008 | frwiki- 2013 | wiki- Talk | cit- Patents | soc-Live Journal1 | ljournal- 2008
계열 1 | -0.19828 | -0.072364 | -0.11014 | -0.0073164 | 0.015521 | 0.30554 | 0.53667 | 0.50416 | 0.18676
More Vertices
Increased
Memory Bandwidth Consumption
Caching very effective
Reduced Memory Bandwidth
Consumption due to
In-Memory Computation

## Slide 289: PEI: PIM-Enabled Instructions: Examples
Executed either in memory or in the processor: dynamic decision
  Low-cost locality monitoring for a single instruction
Cache-coherent, virtually-addressed, single cache block only
Atomic between different PEIs
Not atomic with normal instructions (use pfence for ordering)

## Slide 290: PIM-Enabled Instructions
Key to practicality: single-cache-block restriction
  Each PEI can access at most one last-level cache block
  Similar restrictions exist in atomic instructions
Benefits
  Localization: each PEI is bounded to one memory module
  Interoperability: easier support for cache coherence and virtual memory
  Simplified locality monitoring: data locality of PEIs can be identified simply by the cache control logic

## Slide 291: Example PEI Microarchitecture
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
3D-stacked Memory
…
PCU (PEI Computation Unit)
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU (PEI
Mgmt Unit)
Example PEI uArchitecture

## Slide 292: Evaluated Data-Intensive Applications
Ten emerging data-intensive workloads
  Large-scale graph processing
    Average teenage follower, BFS, PageRank, single-source shortest path, weakly connected components
  In-memory data analytics
    Hash join, histogram, radix partitioning
  Machine learning and data mining
    Streamcluster, SVM-RFE
Three input sets (small, medium, large) for each workload to show the impact of data locality

## Slide 293: PEI Performance Delta: Large Data Sets
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.53918 | 0.31004 | 0.50416 | 0.45845 | 0.47598 | 0.66307 | 0.6314 | 0.44904 | 0.15358 | 0.33671 | 0.4446
Locality-Aware | 0.60067 | 0.34622 | 0.55934 | 0.51064 | 0.5286 | 0.65698 | 0.60316 | 0.44327 | 0.2149 | 0.3438 | 0.47446
(Large Inputs, Baseline: Host-Only)

## Slide 294: PEI Energy Consumption
Chart: 
| Small | Medium | Large
Cache | 0.27613 | 0.22974 | 0.2138
HMC Link | 0.50415 | 0.51297 | 0.51397
DRAM | 0.21457 | 0.25453 | 0.26887
Host-side PCU | 0.0043662 | 0.0036967 | 0.0030358
Memory-side PCU | 0 | 0 | 0
PMU | 7.7323e-05 | 6.4146e-05 | 5.4225e-05
계열 7 | 0.29322 | 0.18897 | 0.14107
계열 8 | 0.68428 | 0.4834 | 0.36147
계열 9 | 0.46391 | 0.35056 | 0.26204
계열 10 | 0 | 0 | 0
계열 11 | 0.015795 | 0.011518 | 0.0085371
계열 12 | 0.0053637 | 0.0036921 | 0.0027686
Host-Only
PIM-Only
Locality-Aware

## Slide 295: More on PIM-Enabled Instructions
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pdf)] [Lightning Session Slides (pdf)]

## Slide 296: More on RowHammer and Memory Reliability

## Slide 297: A Deeper Dive into DRAM Reliability Issues

## Slide 298: Root Causes of Disturbance Errors
Cause 1: Electromagnetic coupling
  Toggling the wordline voltage briefly increases the voltage of adjacent wordlines
  Slightly opens adjacent rows  Charge leakage
Cause 2: Conductive bridges
Cause 3: Hot-carrier injection
Confirmed by at least one manufacturer
Notes: Why do the errors occur? We see three possible causes.
First, there could electromagnetic coupling between adjacent wordlines. When the voltage of one is toggled, it could briefly increase the voltage of the other and facilitate the leakage of charge.
Two other possibilities are conductive bridges and hot-carrier injection.
At least one manufacturer confirmed that these three could play a role in the disturbance errors we see them today.

## Slide 299: RowHammer Characterization Results
Most Modules Are at Risk
Errors vs. Vintage
Error = Charge Loss
Adjacency: Aggressor & Victim
Sensitivity Studies
Other Results in Paper
Solution Space
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)
Notes: Now I will present the characterization results, one-by-one.
First, I show that most modules are at risk. Second, I show the number of errors in a module as a function of the manufacture date. Third, I show that the errors are symptomatic of charge loss. Fourth, I show that an aggressor induces errors in adjacent rows. Fifth, I show several sensitivity studies. And, finally, I briefly describe other results in the paper.

## Slide 300: 4. Adjacency: Aggressor & Victim
Most aggressors & victims are adjacent
Note: For three modules with the most errors (only first bank)
Adjacent
Adjacent
Adjacent
Non-Adjacent
Non-Adjacent
Notes: In this figure, the x-axis is the row-address difference between an aggressor and its victims. And the y-axis is the number of victim-aggressor pairs that correspond to the row-address difference. For all three modules, we see strong peaks at plus/minus 1. This implies that aggressors and victims have consecutive row-addresses, in other words, they are adjacent.
However, the figure also shows some victims that are not adjacent to the aggressor. We believe this could be caused by two reasons. First, depending on the mapping, two rows that are physically adjacent within the DRAM chip may not have consecutive row-addresses. Second, fault rows are often re-mapped to spare rows that may reside on a different portion of the DRAM chip.
Nevertheless, we conclude that the vast majority of aggressors & victims are adjacent.

## Slide 301: ❶ Access Interval (Aggressor)
Note: For three modules with the most errors (only first bank)
Not Allowed
Less frequent accesses  Fewer errors
55ns
500ns
Notes: In this figure, the x-axis is the interval at which we access the aggressor. And the y-axis is the number of errors. To comply with the DRAM standard, we employ a default value of 55ns in our experiments. However, as we increase the access-interval, we see that the number of errors decreases. In particular, at 500ns, there are no errors for all three modules.
From this, we conclude that less frequent accesses induce fewer errors.

## Slide 302: ❷ Refresh Interval
Note: Using three modules with the most errors (only first bank)
More frequent refreshes  Fewer errors
~7x frequent
64ms
Notes: In this figure, the x-axis is the refresh-interval. And the y-axis is the number of errors. To comply with the DRAM standard, we employ a default value of 64ms in our experiments. However, as we decrease the refresh-interval, we see that the number of errors decreases. In particular, when the refresh is shortened by 7x, there are no errors for all three modules.
From this, we conclude that more frequent accesses induce fewer errors.

## Slide 303: ❸ Data Pattern
RowStripe
~RowStripe
111111
111111
111111
111111
000000
000000
000000
000000
000000
111111
000000
111111
111111
000000
111111
000000
Solid
~Solid
10x Errors
Errors affected by data stored in other cells
Notes: We tested the modules with four different data-patterns: Solid, inverse Solid, RowStripe, and inverse RowStripe. Solid and inverse Solid give us full coverage since each cell is tested with both 1s and 0s. And the same applies to RowStripe and its inverse.
However, we found that the rowstripe pattern had 10 times as more errors than the solid pattern. We also tested many other data-patterns, including random, but found RowStripe to induce the most errors.
Therefore, we conclude that errors are affected by data stored in other cells due to differences in coupling effects between the cells.

## Slide 304: 6. Other Results (in Paper)
Victim Cells ≠ Weak Cells (i.e., leaky cells)
  Almost no overlap between them
Errors not strongly affected by temperature
  Default temperature: 50°C
  At 30°C and 70°C, number of errors changes <15%
Errors are repeatable
  Across ten iterations of testing, >70% of victim cells had errors in every iteration
Notes: First, we show that victim cells are not weak cells, which are cells that are inherently leaky. According to our experiments, we saw almost no overlap between them.
Second, we show that errors are not strongly affected by temperature. In all of the tests so far, we set the temperature to 50 degrees Celsius. But even when we changed the temperature by 20 degrees, the number of errors changed by less than 15 percent.
Third, we show that errors are repeatable. Across ten iterations of testing, more than 70% of victim cells had errors in every iteration.

## Slide 305: 6. Other Results (in Paper) cont’d
As many as 4 errors per cache-line
  Simple ECC (e.g., SECDED) cannot prevent all errors
Number of cells & rows affected by aggressor
  Victims cells per aggressor: ≤110
  Victims rows per aggressor: ≤9
Cells affected by two aggressors on either side
  Very small fraction of victim cells (<100) have an error when either one of the aggressors is toggled
Notes: Fourth, we show that there are as many as four errors per cacheline. From this, we conclude that simple ECC schemes (for example, SECDED) cannot prevent all errors.
Fifth, we show that the number of cells & rows affected by an aggressor can be as high as 110 or 9, respectively.
Lastly, we show that a very small fraction of victim cells experience an error when either one of the aggressors is toggled.

## Slide 306: Some Potential Solutions
Cost
Make better DRAM chips
Cost, Power
Sophisticated ECC
Power, Performance
Refresh frequently
Cost, Power, Complexity
Access counters
Notes: Here is a list of four potential solutions to disturbance errors: making better DRAM chips, refreshing more frequently, employing sophisticated ECC schemes, and using hardware counters to track the number of accesses to different rows.
However, all of these solutions incur a large overhead in terms cost, power, performance, and/or complexity.

## Slide 307: Naive Solutions
❶ Throttle accesses to same row
  Limit access-interval: ≥500ns
  Limit number of accesses: ≤128K (=64ms/500ns)
❷ Refresh more frequently
  Shorten refresh-interval by ~7x
Both naive solutions introduce significant overhead in performance and power
Notes: Based on what we learned from the sensitivity studies, there are two naive solutions that immediately present themselves.
First, we can throttle accesses to the same row. If the access-interval is greater than 500ns, I showed how errors are not induced. We can achieve the same effect by limiting the maximum number of accesses to the same row to be less than 128K, within a refresh interval.
Second, we can refresh the module more frequently. If the refresh-interval is shortened by 7x, I showed how errors can be prevented.
However, both naive solutions introduce significant overhead in both performance and power. Later on, I will propose a much more efficient solution.

## Slide 308: Apple’s Patch for RowHammer
https://support.apple.com/en-gb/HT204934
HP and Lenovo released similar patches

## Slide 309: Our Solution to RowHammer
PARA: Probabilistic Adjacent Row Activation
Key Idea
  After closing a row, we activate (i.e., refresh) one of its neighbors with a low probability: p = 0.005
Reliability Guarantee
  When p=0.005, errors in one year: 9.4×10-14
  By adjusting the value of p, we can vary the strength of protection against errors
Notes: We provide a more efficient solution, called PARA, which stands for probabilistic adjacent row activation.
The key idea is thus: after closing a row, we activate (i.e., refresh) one of its neighbors with a low probability, for example, p equal to 0.005.
PARA provides a strong reliability guarantee even under the worst-case access patterns to DRAM. When we set p to 0.005, the expected number of errors in one year is 9.4 times 10 to the negative 14. This probability is much lower the failure rate of other hardware components, for example, the hard-disk drive.
And by adjusting the value of p, PARA can provide an arbitrarily strong-degree of protection against errors.

## Slide 310: Advantages of PARA
PARA refreshes rows infrequently
  Low power
  Low performance-overhead
    Average slowdown: 0.20% (for 29 benchmarks)
    Maximum slowdown: 0.75%
PARA is stateless
  Low cost
  Low complexity
PARA is an effective and low-overhead solution to prevent disturbance errors
Notes: PARA has many advantages. Since it refreshes row infrequently, it has low power and low performance-overhead. Simulated across 29 benchmarks, we saw an average of only 0.2% slowdown and a maximum of only 0.75% slowdown.
In addition, due to its stateless nature, PARA has low cost and complexity.
Therefore, PARA is an effective and low-overhead solution to prevent disturbance errors.

## Slide 311: Requirements for PARA
If implemented in DRAM chip
  Enough slack in timing parameters
  Plenty of slack today:
    Lee et al., “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common Case,” HPCA 2015.
    Chang et al., “Understanding Latency Variation in Modern DRAM Chips,” SIGMETRICS 2016.
    Lee et al., “Design-Induced Latency Variation in Modern DRAM Chips,” SIGMETRICS 2017.
    Chang et al., “Understanding Reduced-Voltage Operation in Modern DRAM Devices,” SIGMETRICS 2017.
If implemented in memory controller
  Better coordination between memory controller and DRAM
  Memory controller should know which rows are physically adjacent

## Slide 312: More on RowHammer Analysis
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data]

## Slide 313: Retrospective on RowHammer & Future
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 314: Challenge and Opportunity for Future
Fundamentally
Secure, Reliable, Safe
Computing Architectures

## Slide 315: Future of Main Memory
DRAM is becoming less reliable  more vulnerable

## Slide 316: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 317
Intuition: quadratic increase in capacity
DRAM Reliability Reducing

## Slide 318: Aside: SSD Error Analysis in the Field
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet]

## Slide 319: Future of Main Memory
DRAM is becoming less reliable  more vulnerable
Due to difficulties in DRAM scaling, other problems may also appear (or they may be going unnoticed)
Some errors may already be slipping into the field
  Read disturb errors (Rowhammer)
  Retention errors
  Read errors, write errors
  …
These errors can also pose security vulnerabilities

## Slide 320: DRAM Data Retention Time Failures
Determining the data retention time of a cell/row is getting more difficult
Retention failures may already be slipping into the field

## Slide 321: Analysis of Retention Failures [ISCA’13]
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 322: Two Challenges to Retention Time Profiling
Data Pattern Dependence (DPD) of retention time
Variable Retention Time (VRT) phenomenon

## Slide 323: Two Challenges to Retention Time Profiling
Challenge 1: Data Pattern Dependence (DPD)
  Retention time of a DRAM cell depends on its value and the values of cells nearby it
  When a row is activated, all bitlines are perturbed simultaneously

## Slide 324: Data Pattern Dependence
Electrical noise on the bitline affects reliable sensing of a DRAM cell
The magnitude of this noise is affected by values of nearby cells via
  Bitline-bitline coupling  electrical coupling between adjacent bitlines
  Bitline-wordline coupling  electrical coupling between each bitline and the activated wordline
Notes: If a cell has lost enough charge, this noise can be large enough to cause a failure on a read
(normally, there is enough noise margin to tolerate the coupling noise)

## Slide 325: Data Pattern Dependence
Electrical noise on the bitline affects reliable sensing of a DRAM cell
The magnitude of this noise is affected by values of nearby cells via
  Bitline-bitline coupling  electrical coupling between adjacent bitlines
  Bitline-wordline coupling  electrical coupling between each bitline and the activated wordline
Retention time of a cell depends on data patterns stored in nearby cells
 need to find the worst data pattern to find worst-case retention time
 this pattern is location dependent
Notes: If a cell has lost enough charge, this noise can be large enough to cause a failure on a read
(normally, there is enough noise margin to tolerate the coupling noise)

## Slide 326: Two Challenges to Retention Time Profiling
Challenge 2: Variable Retention Time (VRT)
  Retention time of a DRAM cell changes randomly over time
    a cell alternates between multiple retention time states
  Leakage current of a cell changes sporadically due to a charge trap in the gate oxide of the DRAM cell access transistor
  When the trap becomes occupied, charge leaks more readily from the transistor’s drain, leading to a short retention time
    Called Trap-Assisted Gate-Induced Drain Leakage
  This process appears to be a random process [Kim+ IEEE TED’11]
  Worst-case retention time depends on a random process
     need to find the worst case despite this

## Slide 327: Modern DRAM Retention Time Distribution
Newer device families have more weak cells than older ones
Likely a result of technology scaling
OLDER
NEWER
OLDER
NEWER

## Slide 328: An Example VRT Cell
A cell from E 2Gb chip family

## Slide 329: Variable Retention Time
A 2Gb chip family
Min ret time = Max ret time
Expected if no VRT
Most failing cells
exhibit VRT
Many failing cells jump from
very high retention time to very low

## Slide 330: More on DRAM Retention Analysis
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 331: Industry Is Writing Papers About It, Too

## Slide 332: Industry Is Writing Papers About It, Too

## Slide 333: Mitigation of Retention Issues [SIGMETRICS’14]
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 334: Handling Data-Dependent Failures [DSN’16]
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 335: Handling Data-Dependent Failures [CAL’16]
Samira Khan, Chris Wilkerson, Donghyuk Lee, Alaa R. Alameldeen, and Onur Mutlu, "A Case for Memory Content-Based Detection and Mitigation of Data-Dependent Failures in DRAM" IEEE Computer Architecture Letters (CAL), November 2016.

## Slide 336: Handling Variable Retention Time [DSN’15]
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 337: Handling Both DPD and VRT [ISCA’17]
Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "The Reach Profiler (REAPER): Enabling the Mitigation of DRAM Retention Failures via Profiling at Aggressive Conditions" Proceedings of the 44th International Symposium on Computer Architecture (ISCA), Toronto, Canada, June 2017.
First experimental analysis of (mobile) LPDDR4 chips
Analyzes the complex tradeoff space of retention time profiling
Key idea: enable fast and robust profiling at higher refresh intervals & temp.

## Slide 338: If Time Permits: NAND Flash Vulnerabilities
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" to appear in Proceedings of the IEEE, 2017.
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.
Fukami+, “Improving the Reliability of Chip-Off Forensic Analysis of NAND Flash Memory Devices,” DFRWS EU 2017.
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 339: Overview Paper on Flash Reliability
Yu Cai, Saugata Ghose, Erich F. Haratsch, Yixin Luo, and Onur Mutlu, "Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives" to appear in Proceedings of the IEEE, 2017.

## Slide 340: NAND Flash Memory Reliability and Security

## Slide 341: Overview Paper
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 342: Evolution of NAND Flash Memory
Flash memory is widening its range of applications
  Portable consumer devices, laptop PCs and enterprise servers
Seaung Suk Lee, “Emerging Challenges in NAND Flash Technology”, Flash Summit 2011 (Hynix)
CMOS scaling
More bits per Cell

## Slide 343: Flash Challenges: Reliability and Endurance
E. Grochowski et al., “Future technology challenges for NAND flash and HDD products”, Flash Memory Summit 2012
P/E cycles (required)
P/E cycles (provided)
A few thousand
Writing
the full capacity
of the drive
10 times per day
for 5 years
(STEC)
> 50k P/E cycles

## Slide 344: NAND Flash Memory is Increasingly Noisy
Noisy NAND
Write
Read

## Slide 345: Future NAND Flash-based Storage Architecture
Memory
Signal
Processing
Error
Correction
Raw Bit
Error Rate
Uncorrectable
BER < 10-15
Noisy
High
Lower
Build reliable error models for NAND flash memory
Design efficient reliability mechanisms based on the model
Our Goals:
Better

## Slide 346: NAND Flash Error Model
Noisy NAND
Write
Read
Experimentally characterize and model dominant errors
Neighbor page prog/read (c-to-c interference)
Retention
Erase block
Program page
Write
Read
Cai et al., “Threshold voltage distribution in MLC NAND Flash Memory: Characterization, Analysis, and Modeling”, DATE 2013
Cai et al., “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques”, HPCA 2017
Cai et al., “Flash Correct-and-Refresh: Retention-aware error management for increased flash memory lifetime”, ICCD 2012
Cai et al., “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation”, ICCD 2013
Cai et al., “Neighbor-Cell Assisted Error Correction in MLC NAND Flash Memories”, SIGMETRICS 2014
Cai et al., “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation”, DSN 2015
Cai et al., “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis””, DATE 2012
Cai et al., “Error Analysis and Retention-Aware Error Management for NAND Flash Memory, ITJ 2013
Cai et al., “Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" , HPCA 2015
Luo et al., “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory”, JSAC 2016

## Slide 347: Our Goals and Approach
Goals:
  Understand error mechanisms and develop reliable predictive models for MLC NAND flash memory errors
  Develop efficient error management techniques to mitigate errors and improve flash reliability and endurance
Approach:
  Solid experimental analyses of errors in real MLC NAND flash memory  drive the understanding and models
  Understanding, models, and creativity  drive the new techniques

## Slide 348: Experimental Testing Platform
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017]
Cai et al., FPGA-based Solid-State Drive prototyping platform, FCCM 2011.

## Slide 349: NAND Flash Error Types
Four types of errors [Cai+, DATE 2012]
Caused by common flash operations
  Read errors
  Erase errors
  Program (interference) errors
Caused by flash cell losing charge over time
  Retention errors
    Whether an error happens depends on required retention time
    Especially problematic in MLC flash because threshold voltage window to determine stored value is smaller

## Slide 350: Observations: Flash Error Analysis
retention errors
Raw bit error rate increases exponentially with P/E cycles
Retention errors are dominant (>99% for 1-year ret. time)
Retention errors increase with retention time requirement
P/E Cycles
Raw Bit Error Rate
Cai et al., Error Patterns in MLC NAND Flash Memory, DATE 2012.

## Slide 351: More on Flash Error Analysis
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Dresden, Germany, March 2012. Slides (ppt)

## Slide 352: Solution to Retention Errors
Refresh periodically
Change the period based on P/E cycle wearout
  Refresh more often at higher P/E cycles
Use a combination of in-place and remapping-based refresh

## Slide 353: One Issue: Read Disturb in Flash Memory
All scaled memories are prone to read disturb errors

## Slide 354: NAND Flash Memory Background
Flash Memory
Page 1
Page 0
Page 2
Page 255
……
Page 257
Page 256
Page 258
Page 511
……
……
Page M+1
Page M
Page M+2
Page M+255
……
Flash Controller
Block 0
Block 1
Block N
Read
Pass
Pass
…
Pass
Notes: When we read from one page in a block, we apply a high voltage to all the other pages in the same block. We will explain why later

## Slide 355: Flash Cell Array
Sense Amplifiers
Block X
Page Y
Sense Amplifiers
Row
Column
Notes: Now, let’s zoom in to a single block of flash memory, which consists of an array of flash pages.
Each flash page is written to flash cells located in the same row.
Each row of cells are controlled by the same horizontal wire.
Each column of cells are connected in series with a sense amplifier at the bottom.

## Slide 356: Flash Cell
Floating Gate
Gate
Drain
Source
Floating Gate Transistor
(Flash Cell)
Vth = 2.5 V
Notes: Now let’s zoom in again to look at a single flash cell, or, it can also be called, a floating gate transistor.

## Slide 357: Flash Read
Vread = 2.5 V
Vth = 3 V
Vth = 2 V
1
0
Vread = 2.5 V
Gate
Notes: Now, if we have two flash cells programmed to different threshold voltages, 2V and 3V, we can distinguish them with a read voltage of 2.5V.
When we apply 2.5V to the gate, since the read voltage is higher than the threshold voltage, …
Now if we look back at this example, we can see that the threshold voltage of each flash cell actually represents the value being stored.

## Slide 358: Flash Pass-Through
Vpass = 5 V
Vth = 2 V
1
Vpass = 5 V
Gate
1
Vth = 3 V
Notes: But, for the same cells, when we apply a high voltage to them, regardless of the threshold voltage, any cell will be passed-through.
So we call this voltage pass-through voltage or Vpass

## Slide 359: Read from Flash Cell Array
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.4V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Vread = 2.5 V
Vpass = 5.0 V
Vpass = 5.0 V
Vpass = 5.0 V
1
1
0
0
Correct values for page 2:
Page 1
Page 2
Page 3
Page 4
Pass (5V)
Read (2.5V)
Pass (5V)
Pass (5V)
Notes: Now, let’s look at an example array of flash cells.
In this example, we make up threshold voltage numbers for each cell.
Let’s say we want to read from the second page in this array.
So we apply a read voltage of 2.5 V to the second page
And since all the other pages are connected in series, we apply a high pass-through voltage of 5 V to the other pages.
As we can see, the high pass through voltage switches on all the flash pages being passed-through, allowing the sense amplifier to read the values stored in the second page.
In this case, the correct values …

## Slide 360: Read Disturb Problem: “Weak Programming” Effect
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.4V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Repeatedly read page 3 (or any page other than page 2)
Read (2.5V)
Pass (5V)
Pass (5V)
Pass (5V)
Page 1
Page 2
Page 3
Page 4
Notes: However, the high pass through voltage can generate read disturb problem, which we will introduce now.
When we want to read page 3, instead of page 2, this high pass through voltage now needs to be applied on the 2nd page.
When we repeatedly read page 3, the pass through voltage induces a weak programming effect on the second page.

## Slide 361: Read Disturb Problem: “Weak Programming” Effect
Vread = 2.5 V
Vpass = 5.0 V
Vpass = 5.0 V
Vpass = 5.0 V
0
1
0
0
High pass-through voltage induces “weak-programming” effect
3.0V
3.8V
3.9V
4.8V
3.5V
2.9V
2.1V
2.2V
4.3V
4.6V
1.8V
3.5V
2.3V
1.9V
4.3V
Incorrect values from page 2:
2.4V
2.6V
Page 1
Page 2
Page 3
Page 4
Notes: As the weak programming effect accumulates, the threshold voltage of each flash cell increases, and the threshold voltage state of a cell can be altered.
In this case, when we read page 2 again, we will read incorrect values from page 2, 0001
Flash vendors conservatively set this pass-through voltage to a high voltage.
However, we find in the paper that it is unnecessary to set to this high, and that reducing this voltage by just a bit will reduce read disturb errors significantly in the future.

## Slide 362: Executive Summary
Read disturb errors limit flash memory lifetime today
  Apply a high pass-through voltage (Vpass) to multiple pages on a read
  Repeated application of Vpass can alter stored values in unread pages
We characterize read disturb on real NAND flash chips
  Slightly lowering Vpass greatly reduces read disturb errors
  Some flash cells are more prone to read disturb
Technique 1: Mitigate read disturb errors online
  Vpass Tuning dynamically finds and applies a lowered Vpass per block
  Flash memory lifetime improves by 21%
Technique 2: Recover after failure to prevent data loss
  Read Disturb Oriented Error Recovery (RDR) selectively corrects cells more susceptible to read disturb errors
  Reduces raw bit error rate (RBER) by up to 36%
Notes: When we read data from one page, we have to apply a high voltage to multiple other flash pages that are connected to this page, and we call this high pass-through voltage.
Over time this high pass-through voltage can alter the values stored in unread flash pages. We call this a read disturb error.
For the first time in open literature, we characterize read disturb on real NAND flash chips, and show that read disturb errors exist in today’s flash chips and is expected to increase in the future.
We make two key observations from the characterization.
Using our characterization, we develop two techniques that can help flash memory tolerate such read disturb errors.

## Slide 363: More on Flash Read Disturb Errors
Yu Cai, Yixin Luo, Saugata Ghose, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015.

## Slide 364: Large-Scale Flash SSD Error Analysis
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet] [Coverage on The Register] [Coverage on TechSpot] [Coverage on The Tech Report]

## Slide 365: Another Time: NAND Flash Vulnerabilities
Onur Mutlu, "Error Analysis and Management for MLC NAND Flash Memory" Technical talk at Flash Memory Summit 2014 (FMS), Santa Clara, CA, August 2014. Slides (ppt) (pdf)
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.
Meza+, “A Large-Scale Study of Flash Memory Errors in the Field,” SIGMETRICS 2015.
Luo+, “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory,” IEEE JSAC 2016.
Cai+, “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques,” HPCA 2017.
Fukami+, “Improving the Reliability of Chip-Off Forensic Analysis of NAND Flash Memory Devices,” DFRWS EU 2017.

## Slide 366: Flash Memory Programming Vulnerabilities
Yu Cai, Saugata Ghose, Yixin Luo, Ken Mai, Onur Mutlu, and Erich F. Haratsch, "Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques" Proceedings of the 23rd International Symposium on High-Performance Computer Architecture (HPCA) Industrial Session, Austin, TX, USA, February 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 367: Other Works on Flash Memory

## Slide 368: NAND Flash Error Model
Noisy NAND
Write
Read
Experimentally characterize and model dominant errors
Neighbor page prog/read (c-to-c interference)
Retention
Erase block
Program page
Write
Read
Cai et al., “Threshold voltage distribution in MLC NAND Flash Memory: Characterization, Analysis, and Modeling”, DATE 2013
Cai et al., “Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques”, HPCA 2017
Cai et al., “Flash Correct-and-Refresh: Retention-aware error management for increased flash memory lifetime”, ICCD 2012
Cai et al., “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation”, ICCD 2013
Cai et al., “Neighbor-Cell Assisted Error Correction in MLC NAND Flash Memories”, SIGMETRICS 2014
Cai et al., “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation”, DSN 2015
Cai et al., “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis””, DATE 2012
Cai et al., “Error Analysis and Retention-Aware Error Management for NAND Flash Memory, ITJ 2013
Cai et al., “Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" , HPCA 2015
Luo et al., “Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory”, JSAC 2016

## Slide 369: Threshold Voltage Distribution
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Grenoble, France, March 2013. Slides (ppt)

## Slide 370: Program Interference and Vref Prediction
Yu Cai, Onur Mutlu, Erich F. Haratsch, and Ken Mai, "Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation" Proceedings of the 31st IEEE International Conference on Computer Design (ICCD), Asheville, NC, October 2013. Slides (pptx) (pdf) Lightning Session Slides (pdf)

## Slide 371: Neighbor-Assisted Error Correction
Yu Cai, Gulay Yalcin, Onur Mutlu, Eric Haratsch, Osman Unsal, Adrian Cristal, and Ken Mai, "Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. Slides (ppt) (pdf)

## Slide 372: Data Retention
Yu Cai, Yixin Luo, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)]

## Slide 373: SSD Error Analysis in the Field
First large-scale field study of flash memory errors
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "A Large-Scale Study of Flash Memory Errors in the Field" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Coverage at ZDNet] [Coverage on The Register] [Coverage on TechSpot] [Coverage on The Tech Report]

## Slide 374: Flash Memory Programming Vulnerabilities
Yu Cai, Saugata Ghose, Yixin Luo, Ken Mai, Onur Mutlu, and Erich F. Haratsch, "Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques" Proceedings of the 23rd International Symposium on High-Performance Computer Architecture (HPCA) Industrial Session, Austin, TX, USA, February 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 375: Accurate and Online Channel Modeling
Yixin Luo, Saugata Ghose, Yu Cai, Erich F. Haratsch, and Onur Mutlu, "Enabling Accurate and Practical Online Flash Channel Modeling for Modern MLC NAND Flash Memory" to appear in IEEE Journal on Selected Areas in Communications (JSAC), 2016.

## Slide 376: More on DRAM Refresh

## Slide 377: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 378: Summary: Refresh-Access Parallelization
DRAM refresh interferes with memory accesses
  Degrades system performance and energy efficiency
  Becomes exacerbated as DRAM density increases
Goal: Serve memory accesses in parallel with refreshes to reduce refresh interference on demand requests
Our mechanisms:
  1. Enable more parallelization between refreshes and accesses across different banks with new per-bank refresh scheduling algorithms
  2. Enable serving accesses concurrently with refreshes in the same bank by exploiting parallelism across DRAM subarrays
Improve system performance and energy efficiency for a wide variety of different workloads and DRAM densities
  20.2% and 9.0% for 8-core systems using 32Gb DRAM at low cost
  Very close to the ideal scheme without refreshes
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.

## Slide 379: Refresh Penalty
Processor
Memory Controller
DRAM
Refresh
Read
Data
Capacitor
Access transistor
Refresh delays requests by 100s of ns
Refresh interferes with memory accesses

## Slide 380: Existing Refresh Modes
Time
Per-bank refresh in mobile DRAM (LPDDRx)
Time
All-bank refresh in commodity DRAM (DDRx)
Bank 7
Bank 1
Bank 0
…
Bank 7
Bank 1
Bank 0
…
Refresh
Round-robin order
…
Per-bank refresh allows accesses to other banks while a bank is refreshing

## Slide 381: Shortcomings of Per-Bank Refresh
Problem 1: Refreshes to different banks are scheduled in a strict round-robin order
  The static ordering is hardwired into DRAM chips
  Refreshes busy banks with many queued requests when other banks are idle
Key idea: Schedule per-bank refreshes to idle banks opportunistically in a dynamic order

## Slide 382: Our First Approach: DARP
Dynamic Access-Refresh Parallelization (DARP)
  An improved scheduling policy for per-bank refreshes
  Exploits refresh scheduling flexibility in DDR DRAM
Component 1: Out-of-order per-bank refresh
  Avoids poor static scheduling decisions
  Dynamically issues per-bank refreshes to idle banks
Component 2: Write-Refresh Parallelization
  Avoids refresh interference on latency-critical reads
  Parallelizes refreshes with a batch of writes

## Slide 383: Shortcomings of Per-Bank Refresh
Problem 2: Banks that are being refreshed cannot concurrently serve memory requests
Time
Bank 0
RD
Delayed by refresh
Per-Bank Refresh

## Slide 384: Shortcomings of Per-Bank Refresh
Problem 2: Refreshing banks cannot concurrently serve memory requests
Key idea: Exploit subarrays within a bank to parallelize refreshes and accesses across subarrays
Time
Bank 0
Subarray 1
Subarray 0
RD
Subarray Refresh
Time
Parallelize

## Slide 385: Methodology
100 workloads: SPEC CPU2006, STREAM, TPC-C/H, random access
System performance metric: Weighted speedup
DDR3 Rank
Simulator configurations
Memory Controller
8-core processor
Memory Controller
Bank 7
Bank 1
Bank 0
…
L1 $: 32KB
L2 $: 512KB/core

## Slide 386: Comparison Points
All-bank refresh [DDR3, LPDDR3, …]
Per-bank refresh [LPDDR3]
Elastic refresh [Stuecheli et al., MICRO ‘10]:
  Postpones refreshes by a time delay based on the predicted rank idle time to avoid interference on memory requests
  Proposed to schedule all-bank refreshes without exploiting per-bank refreshes
  Cannot parallelize refreshes and accesses within a rank
Ideal (no refresh)

## Slide 387: System Performance
Chart: DRAM Chip Density
All-Bank | 5.5359 | 5.3024 | 4.8311
Per-Bank | 5.7551 | 5.5256 | 5.0271
Elastic | 5.6343 | 5.3803 | 4.8911
DARP | 5.9537 | 5.8162 | 5.2317
SARP | 5.9777 | 5.9152 | 5.7295
DSARP | 5.9723 | 5.9543 | 5.8059
Ideal | 6.0252 | 6.0252 | 6.0252
7.9%
12.3%
20.2%
1. Both DARP & SARP provide performance gains and combining them (DSARP) improves even more
2. Consistent system performance improvement across DRAM densities (within 0.9%, 1.2%, and 3.8% of ideal)

## Slide 388: Energy Efficiency
3.0%
5.2%
9.0%
Consistent reduction on energy consumption
Chart: DRAM Chip Density
All-Bank | 38.2974 | 40.28 | 44.8967
Per-Bank | 38.0134 | 39.9893 | 44.5521
Elastic | 37.5049 | 39.3169 | 44.1509
DARP | 37.191 | 38.5881 | 43.25
SARP | 37.1096 | 38.322 | 41.0809
DSARP | 37.137 | 38.197 | 40.8495
Ideal | 36.6284 | 36.6284 | 36.6284

## Slide 389: More Information on Refresh-Access Parallelization
Kevin Chang, Donghyuk Lee, Zeshan Chishti, Alaa Alameldeen, Chris Wilkerson, Yoongu Kim, and Onur Mutlu, "Improving DRAM Performance by Parallelizing Refreshes with Accesses" Proceedings of the 20th International Symposium on High-Performance Computer Architecture (HPCA), Orlando, FL, February 2014. [Summary] [Slides (pptx) (pdf)]

## Slide 390: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 391: Most Refreshes Are Unnecessary
Retention Time Profile of DRAM looks like this:

## Slide 392: RAIDR: Eliminating Unnecessary Refreshes
1. Profiling: Profile the retention time of all DRAM rows
2. Binning: Store rows into bins by retention time
 use Bloom Filters for efficient and scalable storage
3. Refreshing: Memory controller refreshes rows in different bins at different rates
 probe Bloom Filters to determine refresh rate of a row
1.25KB storage in controller for 32GB DRAM memory
Can reduce refreshes by ~75%
 reduces energy consumption and improves performance
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 393: RAIDR: Baseline Design
Refresh control is in DRAM in today’s auto-refresh systems
RAIDR can be implemented in either the controller or DRAM

## Slide 394: RAIDR in Memory Controller: Option 1
Overhead of RAIDR in DRAM controller:
1.25 KB Bloom Filters, 3 counters, additional commands issued for per-row refresh (all accounted for in evaluations)

## Slide 395: RAIDR in DRAM Chip: Option 2
Overhead of RAIDR in DRAM chip:
Per-chip overhead: 20B Bloom Filters, 1 counter (4 Gbit chip)
Total overhead: 1.25KB Bloom Filters, 64 counters (32 GB DRAM)

## Slide 396: RAIDR: Results and Takeaways
System: 32GB DRAM, 8-core; SPEC, TPC-C, TPC-H workloads
RAIDR hardware cost: 1.25 kB (2 Bloom filters)
Refresh reduction: 74.6%
Dynamic DRAM energy reduction: 16%
Idle DRAM power reduction: 20%
Performance improvement: 9%
Benefits increase as DRAM scales in density

## Slide 397: DRAM Device Capacity Scaling: Performance
RAIDR performance benefits increase with DRAM chip capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 398: DRAM Device Capacity Scaling: Energy
RAIDR energy benefits increase with DRAM chip capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 399: RAIDR: Eliminating Unnecessary Refreshes
Observation: Most DRAM rows can be refreshed much less often without losing data [Kim+, EDL’09][Liu+ ISCA’13]
Key idea: Refresh rows containing weak cells
more frequently, other rows less frequently
  1. Profiling: Profile retention time of all rows
  2. Binning: Store rows into bins by retention time in memory controller
  Efficient storage with Bloom Filters (only 1.25KB for 32GB memory)
  3. Refreshing: Memory controller refreshes rows in different bins at different rates
Results: 8-core, 32GB, SPEC, TPC-C, TPC-H
  74.6% refresh reduction @ 1.25KB storage
  ~16%/20% DRAM dynamic/idle power reduction
  ~9% performance improvement
  Benefits increase with DRAM capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 400: More on RAIDR
Jamie Liu, Ben Jaiyen, Richard Veras, and Onur Mutlu, "RAIDR: Retention-Aware Intelligent DRAM Refresh" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pdf)

## Slide 401: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 402: Motivation: Understanding Retention
Past works require accurate and reliable measurement of retention time of each DRAM row
  To maintain data integrity while reducing refreshes
Assumption: worst-case retention time of each row can be determined and stays the same at a given temperature
  Some works propose writing all 1’s and 0’s to a row, and measuring the time before data corruption
Question:
  Can we reliably and accurately determine retention times of all DRAM rows?

## Slide 403: Two Challenges to Retention Time Profiling
Data Pattern Dependence (DPD) of retention time
Variable Retention Time (VRT) phenomenon

## Slide 404: An Example VRT Cell
A cell from E 2Gb chip family

## Slide 405: VRT: Implications on Profiling Mechanisms
Problem 1: There does not seem to be a way of determining if a cell exhibits VRT without actually observing a cell exhibiting VRT
  VRT is a memoryless random process [Kim+ JJAP 2010]
Problem 2: VRT complicates retention time profiling by DRAM manufacturers
  Exposure to very high temperatures can induce VRT in cells that were not previously susceptible
   can happen during soldering of DRAM chips
   manufacturer’s retention time profile may not be accurate
One option for future work: Use ECC to continuously profile DRAM online while aggressively reducing refresh rate
  Need to keep ECC overhead in check

## Slide 406: More on DRAM Retention Analysis
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf)

## Slide 407: Tackling Refresh: Solutions
Parallelize refreshes with accesses [Chang+ HPCA’14]
Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Exploit device characteristics
  Exploit data and application characteristics
Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Understand retention time behavior in DRAM [Liu+ ISCA’13]

## Slide 408: Towards an Online Profiling System
Key Observations:
Testing alone cannot detect all possible failures
Combination of ECC and other mitigation techniques is much more effective
  But degrades performance
Testing can help to reduce the ECC strength
  Even when starting with a higher strength ECC
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Notes: Our high-level design for online profiling system is based to thee key observations:

## Slide 409: Towards an Online Profiling System
Run tests periodically after a short interval
at smaller regions of memory
Initially Protect DRAM
with Strong ECC
1
Periodically Test
Parts of DRAM
2
ECC
Test
Test
Test
Mitigate errors and
reduce ECC
3
Notes: Based on these observations, we propose that in an online profiling system,

## Slide 410: More on Online Profiling of DRAM
Samira Khan, Donghyuk Lee, Yoongu Kim, Alaa Alameldeen, Chris Wilkerson, and Onur Mutlu, "The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Austin, TX, June 2014. [Slides (pptx) (pdf)] [Poster (pptx) (pdf)] [Full data sets]

## Slide 411: How Do We Make RAIDR Work in the Presence of the VRT Phenomenon?

## Slide 412: Making RAIDR Work w/ Online Profiling & ECC
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 413: AVATAR
Insight: Avoid retention failures  Upgrade row on ECC error
Observation: Rate of VRT >> Rate of soft error (50x-2500x)
A
B
C
D
E
F
G
H
DRAM Rows
RETENTION
PROFILING
Weak Cell
0
0
1
0
0
0
1
0
Ref. Rate Table
ECC
ECC
ECC
ECC
ECC
ECC
ECC
ECC
1
AVATAR mitigates VRT by increasing refresh rate on error
Scrub
(15 min)
Row protected from future
retention failures

## Slide 414: RESULTS: REFRESH SAVINGS
AVATAR
No VRT
AVATAR reduces refresh by 60%-70%, similar to multi rate refresh but with VRT tolerance
Retention Testing Once a Year can revert refresh saving from 60% to 70%

## Slide 415: SPEEDUP
Speedup
Chart: 
| 8Gb | 16Gb | 32Gb | 64Gb
AVATAR (1yr) | 1.04 | 1.065 | 1.13 | 1.35
NoRefresh | 1.05 | 1.09 | 1.21 | 1.54
AVATAR gets 2/3rd the performance of NoRefresh. More gains at higher capacity nodes

## Slide 416: ENERGY DELAY PRODUCT
Chart: 
| 8Gb | 16Gb | 32Gb | 64Gb
AVATAR (1yr) | 0.95 | 0.88 | 0.75 | 0.52
NoRefresh | 0.91 | 0.83 | 0.68 | 0.41
Energy Delay Product
AVATAR reduces EDP,
Significant reduction at higher capacity nodes

## Slide 417: Making RAIDR Work w/ Online Profiling & ECC
Moinuddin Qureshi, Dae Hyun Kim, Samira Khan, Prashant Nair, and Onur Mutlu, "AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)]

## Slide 418: DRAM Refresh: Summary and Conclusions
DRAM refresh is a critical challenge
  in scaling DRAM technology efficiently to higher capacities
Discussed several promising solution directions
  Parallelize refreshes with accesses [Chang+ HPCA’14]
  Eliminate unnecessary refreshes [Liu+ ISCA’12]
  Reduce refresh rate and detect+correct errors that occur [Khan+ SIGMETRICS’14]
Examined properties of retention time behavior [Liu+ ISCA’13]
  Enable realistic VRT-Aware refresh techniques [Qureshi+ DSN’15]
Many avenues for overcoming DRAM refresh challenges
  Handling DPD/VRT phenomena
  Enabling online retention time profiling and error mitigation
  Exploiting application behavior

## Slide 419: Other Backup Slides

## Slide 420: Acknowledgments
My current and past students and postdocs
  Rachata Ausavarungnirun, Abhishek Bhowmick, Amirali Boroumand, Rui Cai, Yu Cai, Kevin Chang, Saugata Ghose, Kevin Hsieh, Tyler Huberty, Ben Jaiyen, Samira Khan, Jeremie Kim, Yoongu Kim, Yang Li, Jamie Liu, Lavanya Subramanian, Donghyuk Lee, Yixin Luo, Justin Meza, Gennady Pekhimenko, Vivek Seshadri, Lavanya Subramanian, Nandita Vijaykumar, HanBin Yoon, Jishen Zhao, …
My collaborators
  Can Alkan, Chita Das, Phil Gibbons, Sriram Govindan, Norm Jouppi, Mahmut Kandemir, Mike Kozuch, Konrad Lai, Ken Mai, Todd Mowry, Yale Patt, Moinuddin Qureshi, Partha Ranganathan, Bikash Sharma, Kushagra Vaid, Chris Wilkerson, …

## Slide 421: Funding Acknowledgments
NSF
GSRC
SRC
CyLab
AMD, Google, Facebook, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware

## Slide 422: Summary
Business as Usual | Opportunity
RowHammer | Memory controller anticipates and fixes errors
Fixed, frequent refreshes | Heterogeneous refresh rate across memory
Fixed, high latency | Heterogeneous latency in time and space
Slow page copy & initialization | Exploit internal connectivity in memory to move data
Fixed reliability mechanisms | Heterogeneous reliability across time and space
Memory as a dumb device | Memory as an accelerator and autonomous agent
DRAM-only main memory | Emerging memory technologies and hybrid memories
Two-level data storage model | Unified interface to all data
Large timing and error margins | Online adaptation of timing and error margins
Poor performance guarantees | Strong service guarantees and configurable QoS
Fixed policies in controllers | Configurable and programmable memory controllers
… | …

## Slide 423: Some Open Source Tools
Rowhammer
  https://github.com/CMU-SAFARI/rowhammer
Ramulator – Fast and Extensible DRAM Simulator
  https://github.com/CMU-SAFARI/ramulator
MemSim
  https://github.com/CMU-SAFARI/memsim
NOCulator
  https://github.com/CMU-SAFARI/NOCulator
DRAM Error Model
  http://www.ece.cmu.edu/~safari/tools/memerr/index.html
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 424: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 425: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 426: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 427: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 428: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator

## Slide 429: Rethinking Memory Architecture
Compute Capable Memory
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 430: Large DRAM Power in Modern Systems
>40% in POWER7 (Ware+, HPCA’10)
  >40% in GPU (Paul+, ISCA’15)

## Slide 431: Why Is Power Large?
Design of DRAM uArchitecture
  A lot of waste (granularity, latency, …)
High Voltage
  Can we scale it down reliably?
High Frequency
  Can we scale it down with low performance impact?
DRAM Refresh
…

## Slide 432: Memory Dynamic Voltage/Freq. Scaling
Howard David, Chris Fallin, Eugene Gorbatov, Ulf R. Hanebutte, and Onur Mutlu, "Memory Power Management via Dynamic Voltage/Frequency Scaling" Proceedings of the 8th International Conference on Autonomic Computing (ICAC), Karlsruhe, Germany, June 2011. Slides (pptx) (pdf)

## Slide 433: New Memory Architectures
Compute Capable Memory
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 434: Readings on Memory Compression (I)
Gennady Pekhimenko, Vivek Seshadri, Onur Mutlu, Philip B. Gibbons, Michael A. Kozuch, and Todd C. Mowry, "Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches" Proceedings of the 21st International Conference on Parallel Architectures and Compilation Techniques (PACT), Minneapolis, MN, September 2012. Slides (pptx) Source Code

## Slide 435: Readings on Memory Compression (II)
Gennady Pekhimenko, Vivek Seshadri, Yoongu Kim, Hongyi Xin, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "Linearly Compressed Pages: A Low-Complexity, Low-Latency Main Memory Compression Framework" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] Poster (pptx) (pdf)]

## Slide 436: Readings on Memory Compression (III)
Gennady Pekhimenko, Tyler Huberty, Rui Cai, Onur Mutlu, Phillip P. Gibbons, Michael A. Kozuch, and Todd C. Mowry, "Exploiting Compressed Block Size as an Indicator of Future Reuse" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)]

## Slide 437: Readings on Memory Compression (IV)
Gennady Pekhimenko, Evgeny Bolotin, Nandita Vijaykumar, Onur Mutlu, Todd C. Mowry, and Stephen W. Keckler, "A Case for Toggle-Aware Compression for GPU Systems" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)]

## Slide 438: Readings on Memory Compression (V)
Nandita Vijaykumar, Gennady Pekhimenko, Adwait Jog, Abhishek Bhowmick, Rachata Ausavarungnirun, Chita Das, Mahmut Kandemir, Todd C. Mowry, and Onur Mutlu, "A Case for Core-Assisted Bottleneck Acceleration in GPUs: Enabling Flexible Data Compression with Assist Warps" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 439: Emerging Technologies and Hybrid Memories

## Slide 440: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Data stored by changing phase of material
  Data read by detecting material’s resistance
  Expected to scale to 9nm (2022 [ITRS 2009])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have (many) shortcomings
  Can they be enabled to replace/augment/surpass DRAM?
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 441: Solution 2: Emerging Memory Technologies
Lee+, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA’09, CACM’10, IEEE Micro’10.
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters 2012.
Yoon, Meza+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012.
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Lu+, “Loose Ordering Consistency for Persistent Memory,” ICCD 2014.
Zhao+, “FIRM: Fair and High-Performance Memory Control for Persistent Memory Systems,” MICRO 2014.
Yoon, Meza+, “Efficient Data Mapping and Buffering Techniques for Multi-Level Cell Phase-Change Memories,” TACO 2014.
Ren+, “ThyNVM: Enabling Software-Transparent Crash Consistency in Persistent Memory Systems,” MICRO 2015.
Chauhan+, “NVMove: Helping Programmers Move to Byte-Based Persistence,” INFLOW 2016.
Li+, “Utility-Based Hybrid Memory Management,” CLUSTER 2017.
Yu+, “Banshee: Bandwidth-Efficient DRAM Caching via Software/Hardware Cooperation,” MICRO 2017.
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 442: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 443: What is Phase Change Memory?
Phase change material (chalcogenide glass) exists in two states:
  Amorphous: Low optical reflexivity and high electrical resistivity
  Crystalline: High optical reflexivity and low electrical resistivity
PCM is resistive memory: High resistance (0), Low resistance (1)
PCM cell can be switched between states reliably and quickly

## Slide 444: How Does PCM Work?
Write: change phase via current injection
  SET: sustained current to heat cell above Tcryst
  RESET: cell heated above Tmelt and quenched
Read: detect phase via material resistance
  amorphous/crystalline
Large
Current
SET (cryst)
Low resistance
103-104 W
Small
Current
RESET (amorph)
High resistance
Access
Device
Memory
Element
106-107 W
Photo Courtesy: Bipin Rajendran, IBM
Slide Courtesy: Moinuddin Qureshi, IBM

## Slide 445: Opportunity: PCM Advantages
Scales better than DRAM, Flash
  Requires current pulses, which scale linearly with feature size
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
Can be denser than DRAM
  Can store multiple bits per cell due to large resistance range
  Prototypes with 2 bits/cell in ISSCC’08, 4 bits/cell by 2012
Non-volatile
  Retain data for >10 years at 85C
No refresh needed, low idle power

## Slide 446: Phase Change Memory Properties
Surveyed prototypes from 2003-2008 (ITRS, IEDM, VLSI, ISSCC)
Derived PCM parameters for F=90nm
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
Lee et al., “Phase Change Technology and the Future of Main Memory,” IEEE Micro Top Picks 2010.

## Slide 448: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 449: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 450: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 451: Architecting PCM to Mitigate Shortcomings
Idea 1: Use multiple narrow row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 2: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 452: More on PCM As Main Memory
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf)

## Slide 453: More on PCM As Main Memory (II)
Benjamin C. Lee, Ping Zhou, Jun Yang, Youtao Zhang, Bo Zhao, Engin Ipek, Onur Mutlu, and Doug Burger, "Phase Change Technology and the Future of Main Memory" IEEE Micro, Special Issue: Micro's Top Picks from 2009 Computer Architecture Conferences (MICRO TOP PICKS), Vol. 30, No. 1, pages 60-70, January/February 2010.

## Slide 454: Data Placement in Hybrid Memory
Memory A is fast, but small
Load should be balanced on both channels
Page migrations have performance and energy overhead
Channel A
Channel B
Memory A
Memory B
(Fast, Small)
(Large, Slow)
Page 1
Page 2
IDLE
Which memory do we place each page in,
to maximize system performance?
Cores/Caches
Memory Controllers

## Slide 455: Data Placement Between DRAM and PCM
Idea: Characterize data access patterns and guide data placement in hybrid memory
Streaming accesses: As fast in PCM as in DRAM
Random accesses: Much faster in DRAM
Idea: Place random access data with some reuse in DRAM; streaming data in PCM
Yoon+, “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.

## Slide 456: Hybrid vs. All-PCM/DRAM [ICCD’12]
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
31% better performance than all PCM,
within 29% of all DRAM performance
31%
29%
Yoon+, “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 457: More on Hybrid Memory Data Placement
HanBin Yoon, Justin Meza, Rachata Ausavarungnirun, Rachael Harding, and Onur Mutlu, "Row Buffer Locality Aware Caching Policies for Hybrid Memories" Proceedings of the 30th IEEE International Conference on Computer Design (ICCD), Montreal, Quebec, Canada, September 2012. Slides (pptx) (pdf)

## Slide 458: Weaknesses of Existing Solutions
They are all heuristics that consider only a limited part of memory access behavior
Do not directly capture the overall system performance impact of data placement decisions
Example: None capture memory-level parallelism (MLP)
  Number of concurrent memory requests from the same application when a page is accessed
  Affects how much page migration helps performance
Notes: These proposals consider only a limited number of characteristics, using these few data points to construct a placement heuristic that is specific to the memory types being used in the system.
These heuristic-based approaches do not directly capture the overall system performance benefits of data placement decisions.
Therefore, they can only indirectly optimize system performance, which sometimes leads to sub-optimal data placement decisions.

## Slide 459: Importance of Memory-Level Parallelism
requests to Page 1
requests to Page 3
requests to Page 1
requests to Page 3
time
Before migration:
After migration:
requests to Page 2
requests to Page 2
time
Before migration:
After migration:
Mem. B
Mem. B
Mem. A
Mem. A
Mem. B
Mem. A
T
T
Migrating one page reduces stall time by T
Must migrate two pages to reduce stall time by T:
migrating one page alone does not help
Mem. B
Page migration decisions need to consider MLP
Notes: Should say: On the left, The page has much more utility because it directly affects performance if it is migrated to the fast memory;
On the right. Each page has less utility because migrated alone, neither would affect performance significantly. They both need to be migrated together.
Let’s look at two pages with access latency overlapped with each other
Change animation later

## Slide 460: Our Goal [CLUSTER 2017]
A generalized mechanism that
1. Directly estimates the performance benefit of migrating a page between any two types of memory
2. Places only the performance-critical data in the fast memory

## Slide 461: Utility-Based Hybrid Memory Management
A memory manager that works for any hybrid memory
  e.g., DRAM-NVM, DRAM-RLDRAM
Key Idea
  For each page, use comprehensive characteristics to calculate estimated utility (i.e., performance impact) of migrating page from one memory to the other in the system
  Migrate only pages with the highest utility (i.e., pages that improve system performance the most when migrated)
Li+, “Utility-Based Hybrid Memory Management”, CLUSTER 2017.

## Slide 462: Key Mechanisms of UH-MEM
For each page, estimate utility using a performance model
  Application stall time reduction
    How much would migrating a page benefit the performance of the application that the page belongs to?
  Application performance sensitivity
    How much does the improvement of a single application’s performance increase the overall system performance?
Migrate only pages whose utility exceed the migration threshold from slow memory to fast memory
Periodically adjust migration threshold

## Slide 463: Results: System Performance
Chart: Workload Memory Intensity Category
| 0.0 | 0.25 | 0.5 | 0.75 | 1.0
ALL | 1 | 1 | 1 | 1 | 1
FREQ | 1.09 | 1.06 | 1.1 | 1.22 | 1.39
RBLA | 1.09 | 1.09 | 1.11 | 1.26 | 1.42
UH-MEM | 1.09 | 1.12 | 1.16 | 1.37 | 1.61
14%
5%
3%
9%
UH-MEM improves system performance
over the best state-of-the-art hybrid memory manager

## Slide 464: Results: Sensitivity to Slow Memory Latency
We vary and of the slow memory
Chart: Slow Memory Latency Multiplier
| x3.0 x3.0 | x4.0 x4.0 | x4.5 x12 | x6.0 x16 | x7.5 x20
ALL | 2.13 | 2.12 | 2.1 | 2.08 | 2.06
FREQ | 3.2 | 3.14 | 2.91 | 2.74 | 2.57
RBLA | 3.33 | 3.27 | 2.99 | 2.86 | 2.79
UH-MEM | 3.6 | 3.45 | 3.39 | 3.23 | 3.15
13%
13%
8%
6%
14%
UH-MEM improves system performance for a wide variety of hybrid memory systems

## Slide 465: Crash Consistency

## Slide 466: One Key Challenge in Persistent Memory
How to ensure consistency of system/data if all memory is persistent?
Two extremes
  Programmer transparent: Let the system handle it
  Programmer only: Let the programmer handle it
Many alternatives in-between…

## Slide 467: CHALLENGE: CRASH CONSISTENCY
System crash can result in
permanent data corruption in NVM
Persistent Memory System

## Slide 468: CRASH CONSISTENCY PROBLEM
Example: Add a node to a linked list
1. Link to next
2. Link to prev
System crash can result in
inconsistent memory state
Notes: Let’s see an example of crash consistency problem in persistent memory systems. When we add a node in the linked list, there are two operations, first, we need to link the new node to next node and then link the previous node to the new node. Unfortunately due to the write ordering, we cannot guarantee which write will reach the memory first. If there is a power failure, depending on which write persisted, we might have a broken linked list. As a result, after a crash we can have an inconsistent memory state.

## Slide 469: CURRENT SOLUTIONS
Explicit interfaces to manage consistency
  NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]
AtomicBegin {
Insert a new node;
} AtomicEnd;
Limits adoption of NVM
Have to rewrite code with clear partition
between volatile and non-volatile data
Burden on the programmers

## Slide 470: OUR APPROACH: ThyNVM
Goal:
Software transparent consistency in
persistent memory systems

## Slide 471: ThyNVM: Summary
Checkpoints at multiple granularities to reduce both checkpointing latency and metadata overhead
Overlaps checkpointing and execution to reduce checkpointing latency
Adapts to DRAM and NVM characteristics
Performs within 4.9% of an idealized DRAM with zero cost consistency
A new hardware-based
checkpointing mechanism

## Slide 472: End of Backup Slides

## Slide 473: Brief Self Introduction
Onur Mutlu
  Full Professor @ ETH Zurich CS, since September 2015
  Strecker Professor @ Carnegie Mellon University ECE/CS, 2009-2016, 2016-…
  PhD from UT-Austin, worked @ Google, VMware, Microsoft Research, Intel, AMD
  https://people.inf.ethz.ch/omutlu/
  omutlu@gmail.com (Best way to reach me)
  https://people.inf.ethz.ch/omutlu/projects.htm
Research, Education, Consulting in
  Computer architecture and systems, bioinformatics
  Memory and storage systems, emerging technologies
  Many-core systems, heterogeneous systems, core design
  Interconnects
  Hardware/software interaction and co-design (PL, OS, Architecture)
  Predictable and QoS-aware systems
  Hardware fault tolerance and security
  Algorithms and architectures for genome analysis
  …