## Slide 1: Intelligent Architectures for Intelligent Machines
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
1 October 2022
INSAIT Conference

## Slide 2: How Intelligent Are Our Platforms?
Source: https://taxistartup.com/wp-content/uploads/2015/03/UK-Self-Driving-Cars.jpg

## Slide 3: The Problem
Computing
is Bottlenecked by Data

## Slide 4: Data is Key for AI, ML, Genomics, …
Important workloads are all data intensive
They require rapid and efficient processing of large amounts of data
Data is increasing
  We can generate more than we can process

## Slide 5: Huge Demand for Performance & Efficiency
https://www.youtube.com/watch?v=x2-qB0J7KHw

## Slide 6: Data is Key for Future Workloads
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 7: Data Overwhelms Modern Machines
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Data → performance & energy bottleneck

## Slide 8
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data is Key for Future Workloads
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 9
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 10: Data is Key for Future Workloads
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 11
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Medical Treatment &
Scientific Discovery
Data → performance & energy bottleneck
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 12: We Need Faster & Scalable Genome Analysis
Predicting the presence and relative abundance of microbes in a sample
Understanding genetic variations, species, evolution, …
Rapid surveillance of disease outbreaks
Developing personalized medicine
And, many, many other applications …
Notes: Knowing what organisms are present in a given environmental sample and how abundant are they

## Slide 13: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version]
Oxford Nanopore MinION

## Slide 14: New Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Preliminary arxiv.org version]
Oxford Nanopore MinION
Data → performance & energy bottleneck

## Slide 15: One Problem with (Genome) Analysis Today
Special-Purpose Machine
for Data Generation
General-Purpose Machine
for Data Analysis
FAST SLOW
Slow and inefficient processing capability
This picture is similar for many “data generators & analyzers” today

## Slide 16: Accelerating Genome Analysis [IEEE MICRO 2020]
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 17: FPGA-based Near-Memory Analytics
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gómez-Luna, Henk Corporaal, and Onur Mutlu, "FPGA-based Near-Memory Acceleration of Modern Data-Intensive Applications" IEEE Micro (IEEE MICRO), 2021.

## Slide 18: Beginner Reading on Genome Analysis
Mohammed Alser, Joel Lindegger, Can Firtina, Nour Almadhoun, Haiyu Mao, Gagandeep Singh, Juan Gomez-Luna, Onur Mutlu
“From Molecules to Genomic Variations to Scientific Discovery: Intelligent Algorithms and Architectures for Intelligent Genome Analysis”
Computational and Structural Biotechnology Journal, 2022
[Source code]
https://arxiv.org/pdf/2205.07957.pdf

## Slide 19: Data Overwhelms Modern Machines …
Storage/memory capability
Communication capability
Computation capability
Greatly impacts robustness, energy, performance, cost

## Slide 20: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 21: Perils of Processor-Centric Design
Most of the system is dedicated to storing and moving data
Yet, system is still bottlenecked by memory

## Slide 22: Deeper and Larger Memory Hierarchies
https://wccftech.com/amd-ryzen-5000-zen-3-vermeer-undressed-high-res-die-shots-close-ups-pictured-detailed/
AMD Ryzen 5000, 2020
Core Count:
8 cores/16 threads
L1 Caches:
32 KB per core
L2 Caches:
512 KB per core
L3 Cache:
32 MB shared

## Slide 23: AMD’s 3D Last Level Cache (2021)
https://youtu.be/gqAYMx34euU
https://www.tech-critter.com/amd-keynote-computex-2021/
https://community.microcenter.com/discussion/5134/comparing-zen-3-to-zen-2
Additional 64 MB L3 cache die stacked on top of the processor die
- Connected using Through Silicon Vias (TSVs)
- Total of 96 MB L3 cache
AMD increases the L3 size of their 8-core Zen 3 processors from 32 MB to 96 MB
Notes: CCD = Core Chiplet Die
Structural silicon is used to equalize the height and facilitate heat dissipation from the cores.

## Slide 24: Deeper and Larger Memory Hierarchies
https://www.it-techblog.de/ibm-power10-prozessor-mehr-speicher-mehr-tempo-mehr-sicherheit/09/2020/
IBM POWER10,
2020
Cores:
15-16 cores,
8 threads/core
L2 Caches:
2 MB per core
L3 Cache:
120 MB shared

## Slide 25: Deeper and Larger Memory Hierarchies
https://www.gsmarena.com/apple_announces_m1_ultra_with_20core_cpu_and_64core_gpu-news-53481.php
Apple M1 Ultra System (2022)
DRAM
DRAM
A lot of
Cache
Storage
Storage

## Slide 26
  Chrome
    Google’s web browser
TensorFlow Mobile
Google’s machine learning framework
  Video Playback
Google’s video codec
  Video Capture
Google’s video codec
Data Overwhelms Modern Machines
Data → performance & energy bottleneck
Notes: In this work, we take a look at widely-used google consumer workloads, to figure out the major sources of energy consumption.
We look at Google Chrome web brower. We take a look at Tensorflow, Google’s machine learning framework, and we also take a look at two important video related workloads, video playback and video capture, both rely on Google’s vp9 codec technology.

## Slide 27
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement
Data Movement Overwhelms Modern Machines

## Slide 28: Axiom
An Intelligent Architecture
Handles Data Well

## Slide 29: How to Handle Data Well
Ensure data does not overwhelm the components
  via intelligent algorithms, architectures & system designs: algorithm-architecture-devices
Take advantage of vast amounts of data and metadata
  to improve architectural & system-level decisions
Understand and exploit properties of (different) data
  to improve algorithms & architectures in various metrics

## Slide 30: Corollaries: Computing Systems Today …
Are processor-centric vs. data-centric
Make designer-dictated decisions vs. data-driven
Make component-based myopic decisions vs. data-aware

## Slide 31: Architectures for Intelligent Machines
Data-centric
Data-driven
Data-aware

## Slide 32: A Blueprint for Fundamentally Better Architectures
Onur Mutlu, "Intelligent Architectures for Intelligent Computing Systems" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Virtual, February 2021. [Slides (pptx) (pdf)] [IEDM Tutorial Slides (pptx) (pdf)] [Short DATE Talk Video (11 minutes)] [Longer IEDM Tutorial Video (1 hr 51 minutes)]

## Slide 33: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 34: Data-Centric (Memory-Centric) Architectures

## Slide 35: Data-Centric Architectures: Properties
Process data where it resides (where it makes sense)
  Processing in and near memory & sensor structures
Low-latency & low-energy data access
Low-cost data storage & processing
Intelligent data management

## Slide 36: Processing Data Where It Makes Sense

## Slide 37: Process Data Where It Makes Sense
https://www.gsmarena.com/apple_announces_m1_ultra_with_20core_cpu_and_64core_gpu-news-53481.php
Apple M1 Ultra System (2022)
DRAM
DRAM
A lot of
Cache
Storage
Storage
Sensors

## Slide 38: Processing in Memory: An Old Idea
Kautz, “Cellular Logic-in-Memory Arrays”, IEEE TC 1969.
https://doi.org/10.1109/T-C.1969.222754

## Slide 39: Processing in Memory: An Old Idea
Stone, “A Logic-in-Memory Computer,” IEEE TC 1970.
https://safari.ethz.ch/architecture/fall2020/lib/exe/fetch.php?media=stone_logic_in_memory_1970.pdf

## Slide 40: Why In-Memory Computation Today?
Huge problems with Memory Technology
  Memory technology scaling is not going well (e.g., RowHammer)
  Many scaling issues demand intelligence in memory
Huge demand from Applications & Systems
  Data access bottleneck
  Energy & power bottlenecks
  Data movement energy dominates computation energy
  Need all at the same time: performance, energy, sustainability
  We can improve all metrics by minimizing data movement
Designs are squeezed in the middle

## Slide 41: Processing-in-Memory Landscape Today
[UPMEM 2019]
[Samsung 2021]
[SK Hynix 2022]
[Samsung 2021]
And, many other experimental chips and startups
[Alibaba 2022]

## Slide 42: Memory Scaling Issues Are Real
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Proceedings of the 5th International Memory Workshop (IMW), Monterey, CA, May 2013. Slides (pptx) (pdf) EETimes Reprint
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 43: Infrastructures to Understand Such Issues
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 44: Memory Testing Infrastructures
* SoftMC [Hassan+, HPCA’17] enhanced for DDR4
Notes: We implement U-TRR using SoftMC, an FPGA-based infrastructure with precise temperature control which we enhanced for DDR4

## Slide 45: Updated Memory Testing Infrastructure
  FPGA-based SoftMC (Xilinx Virtex UltraScale+ XCU200)
Fine-grained control over DRAM commands,
timing (±1.5ns), temperature (±0.1°C ),
and voltage (±1mV)
*Hassan et al., "SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies," in HPCA, 2017. [Available on GitHub: https://github.com/CMU-SAFARI/SoftMC]
*
Notes: We use an FPGA-based experimental setup programmed with a modified version of SoftMC [CLICK]
We control the chip temperature using a pair of heaters [CLICK] connected to a temperature controller [CLICK]
We supply the wordline voltage using the VPP power rail from an external power supply [CLICK]
This infrastructure provides fine-grained control over DRAM commands, timing parameters, temperature, and wordline voltage [CLICK]
=======

## Slide 46: A Curious Phenomenon [Kim et al., ISCA 2014]
One can
predictably induce errors
in most DRAM memory chips
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.

## Slide 47: RowHammer
A simple hardware failure mechanism
can create a widespread
system security vulnerability

## Slide 48
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 49: Memory Scaling Issues Are Real
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 50: Memory Scaling Issues Are Real
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version] [Slides from COSADE 2019 (pptx)] [Slides from VLSI-SOC 2020 (pptx) (pdf)] [Talk Video (1 hr 15 minutes, with Q&A)]

## Slide 51: The Story of RowHammer Tutorial …
Onur Mutlu, "Security Aspects of DRAM: The Story of RowHammer" Invited Tutorial at 14th IEEE Electron Devices Society International Memory Workshop (IMW), Dresden, Germany, May 2022. [Slides (pptx)(pdf)] [Tutorial Video (57 minutes)]
https://www.youtube.com/watch?v=37hWglkQRG0

## Slide 52: 10 Years of RowHammer in 20 Minutes
Onur Mutlu, "The Story of RowHammer" Invited Talk at the Workshop on Robust and Safe Software 2.0 (RSS2), held with the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, 28 February 2022. [Slides (pptx) (pdf)]
https://www.youtube.com/watch?v=ctKTRyi96Bk

## Slide 53: The Push from Circuits and Devices
Main Memory Needs
Intelligent Controllers

## Slide 54: Intel Optane Persistent Memory (2019)
Non-volatile main memory
Based on 3D-XPoint Technology
https://www.storagereview.com/intel_optane_dc_persistent_memory_module_pmm

## Slide 55: Emerging Memories Also Need Intelligent Controllers
Benjamin C. Lee, Engin Ipek, Onur Mutlu, and Doug Burger, "Architecting Phase Change Memory as a Scalable DRAM Alternative" Proceedings of the 36th International Symposium on Computer Architecture (ISCA), pages 2-13, Austin, TX, June 2009. Slides (pdf) One of the 13 computer architecture papers of 2009 selected as Top Picks by IEEE Micro. Selected as a CACM Research Highlight. 2022 Persistent Impact Prize.

## Slide 56: The Takeaway
Intelligent
Memory Controllers
Can Avoid Many Failures
& Enable Better Scaling

## Slide 57: Three Key Systems & Application Trends
1. Data access is the major bottleneck
  Applications are increasingly data hungry
2. Energy consumption is a key limiter
3. Data movement energy dominates compute
  Especially true for off-chip to on-chip movement

## Slide 58: Do We Want This?
Source: V. Milutinovic

## Slide 59: Or This?
Source: V. Milutinovic

## Slide 60: Challenge and Opportunity for Future
High Performance,
Energy Efficient,
Sustainable
(All at the Same Time)

## Slide 61: The Problem
Data access is the major performance and energy bottleneck
Our current
design principles
cause great energy waste
(and great performance loss)

## Slide 62: The Problem
Processing of data
is performed
far away from the data

## Slide 63: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 64: A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 65: Today’s Computing Systems
Processor centric
All data processed in the processor  at great system cost

## Slide 66: It’s the Memory, Stupid!
“It’s the Memory, Stupid!” (Richard Sites, MPR, 1996)
http://cva.stanford.edu/classes/cs99s/papers/architects_look_to_future.pdf

## Slide 67: The Performance Perspective
Mutlu+, “Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-Order Processors,” HPCA 2003.

## Slide 68: The Performance Perspective
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors" Proceedings of the 9th International Symposium on High-Performance Computer Architecture (HPCA), pages 129-140, Anaheim, CA, February 2003. Slides (pdf)
  One of the 15 computer arch. papers of 2003 selected as Top Picks by IEEE Micro. HPCA Test of Time Award (awarded in 2021).

## Slide 69: The Performance Perspective (Today)
All of Google’s Data Center Workloads (2015):
Kanev+, “Profiling a Warehouse-Scale Computer,” ISCA 2015.

## Slide 70: The Energy Perspective
Dally, HiPEAC 2015

## Slide 71: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 72: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.

## Slide 73: Data Movement vs. Computation Energy
Chart: Energy for a 32-bit Operation (log scale)
| ADD (int) | ADD (float) | Register File | MULT (int) | MULT (float) | SRAM Cache | DRAM
Energy (pJ) | 0.1 | 0.9 | 1 | 3.1 | 3.7 | 5 | 640
ADD (int) Relative Cost | 1 | 9 | 10 | 31 | 37 | 50 | 6400
Han+, “EIE: Efficient Inference Engine on Compressed Deep Neural Network,” ISCA 2016.
6400X
A memory access consumes 6400X
the energy of a simple integer addition

## Slide 74: Energy Waste in Mobile Devices
Amirali Boroumand, Saugata Ghose, Youngsok Kim, Rachata Ausavarungnirun, Eric Shiu, Rahul Thakur, Daehyun Kim, Aki Kuusela, Allan Knies, Parthasarathy Ranganathan, and Onur Mutlu, "Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks" Proceedings of the 23rd International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Williamsburg, VA, USA, March 2018.
62.7% of the total system energy
is spent on data movement

## Slide 75: We Do Not Want to Move Data!
Dally, HiPEAC 2015
A memory access consumes ~100-1000X
the energy of a complex addition

## Slide 76: We Need A Paradigm Shift To …
Enable computation with minimal data movement
Compute where it makes sense (where data resides)
Make computing architectures more data-centric

## Slide 77: Goal: Processing Inside Memory
Many questions … How do we design the:
  compute-capable memory & controllers?
  processors & communication units?
  software & hardware interfaces?
  system software, compilers, languages?
  algorithms & theoretical foundations?
Cache
Processor
Core
Interconnect
Memory
Database
Graphs
Media
Query
Results
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons

## Slide 78: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 79: We Need to Think Differently from the Past Approaches

## Slide 80: Processing in Memory: Two Approaches
1. Processing near Memory
2. Processing using Memory

## Slide 81: Mindset: Memory as an Accelerator
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 82: Accelerating In-Memory Graph Analytics
Large graphs are everywhere (circa 2015)
Scalable large-scale graph processing is challenging
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos
Chart: Speedup
| 128 Cores | 32 Cores
열3 | 1.4206 | 1

## Slide 83: Key Bottlenecks in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 84: Opportunity: 3D-Stacked Logic+Memory
Logic
Memory
Other “True 3D” technologies
under development

## Slide 85: Tesseract System for Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Interconnected set of 3D-stacked memory+logic chips with simple cores
Logic
Memory
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 86: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communications via Remote Function Calls

## Slide 87: Tesseract System for Graph Processing
Logic
Memory
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 88: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
Tesseract
32 Tesseract Cores
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 89: Tesseract Graph Processing Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
>13X Performance Improvement
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.
On five graph processing algorithms

## Slide 90: Tesseract Graph Processing System Energy
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
> 8X Energy Reduction
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing” ISCA 2015.

## Slide 91: More on Tesseract
Junwhan Ahn, Sungpack Hong, Sungjoo Yoo, Onur Mutlu, and Kiyoung Choi, "A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing" Proceedings of the 42nd International Symposium on Computer Architecture (ISCA), Portland, OR, June 2015. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] Top Picks Honorable Mention by IEEE Micro.

## Slide 92: In-Storage Genomic Data Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)] [Talk Video (17 minutes)]

## Slide 93: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement from Storage
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 94: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 95: Key Idea
Storage
System
Filter out Non-matching reads
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Filter out Exactly-matching reads
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 96: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 97: GenStore Talk Video
https://www.youtube.com/watch?v=kIU44FxjbFk

## Slide 98: In-Storage Genomic Data Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 99: Eliminating the Adoption Barriers
Processing-in-Memory
in the Real World

## Slide 100: Processing-in-Memory Landscape Today
[UPMEM 2019]
[Samsung 2021]
[SK Hynix 2022]
[Samsung 2021]
This does not include many experimental chips and startups
[Alibaba 2022]

## Slide 101: UPMEM Processing in Memory Modules
E19: 8 chips DIMM (1 rank). DRAM PUs @ 267 MHz
P21: 16 chips DIMM (2 ranks). DRAM PUs @ 350 MHz
www.upmem.com

## Slide 102: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 103: More on the UPMEM PIM System
https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=26

## Slide 104: UPMEM PIM System Summary & Analysis
Juan Gomez-Luna, Izzat El Hajj, Ivan Fernandez, Christina Giannoula, Geraldo F. Oliveira, and Onur Mutlu, "Benchmarking Memory-Centric Computing Systems: Analysis of Real Processing-in-Memory Hardware" Invited Paper at Workshop on Computing with Unconventional Technologies (CUT), Virtual, October 2021. [arXiv version] [PrIM Benchmarks Source Code] [Slides (pptx) (pdf)] [Talk Video (37 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 105: PrIM Benchmarks: Application Domains
Domain | Benchmark | Short name
Dense linear algebra | Vector Addition | VA
 | Matrix-Vector Multiply | GEMV
Sparse linear algebra | Sparse Matrix-Vector Multiply | SpMV
Databases | Select | SEL
 | Unique | UNI
Data analytics | Binary Search | BS
 | Time Series Analysis | TS
Graph processing | Breadth-First Search | BFS
Neural networks | Multilayer Perceptron | MLP
Bioinformatics | Needleman-Wunsch | NW
Image processing | Image histogram (short) | HST-S
 | Image histogram (large) | HST-L
Parallel primitives | Reduction | RED
 | Prefix sum (scan-scan-add) | SCAN-SSA
 | Prefix sum (reduce-scan-scan) | SCAN-RSS
 | Matrix transposition | TRNS

## Slide 106: PrIM Benchmarks are Open Source
All microbenchmarks, benchmarks, and scripts
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 107: Understanding a Modern PIM Architecture
https://arxiv.org/pdf/2105.03814.pdf
https://github.com/CMU-SAFARI/prim-benchmarks

## Slide 108: ML Training on a Real PIM System
Short version: https://arxiv.org/pdf/2206.06022.pdf
Long version: https://arxiv.org/pdf/2207.07886.pdf
https://www.youtube.com/watch?v=qeukNs5XI3g&t=11226s

## Slide 109: ML Training on a Real PIM System
Need to optimize data representation
  (1) fixed-point
  (2) quantization
  (3) hybrid precision
Use lookup tables (LUTs) to implement complex functions (e.g., sigmoid)
Optimize data placement & layout for streaming access
Large speedups: 2.8X/27X vs. CPU, 1.3x/3.2x vs. GPU

## Slide 110: ML Training on Real PIM Talk Video
https://www.youtube.com/watch?v=qeukNs5XI3g&t=11226s

## Slide 111: Samsung Function-in-Memory DRAM (2021)
https://news.samsung.com/global/samsung-develops-industrys-first-high-bandwidth-memory-with-ai-processing-power

## Slide 112: Samsung Function-in-Memory DRAM (2021)

## Slide 113: Samsung Function-in-Memory DRAM (2021)

## Slide 114: Samsung Function-in-Memory DRAM (2021)

## Slide 115: Samsung & Meta AxDIMM (2021)
DDRx-PIM
  Deep learning recommendation system
Baseline System
AxDIMM System
Ke et al. "Near-Memory Processing in Action: Accelerating Personalized Recommendation with AxDIMM", IEEE Micro (2021)

## Slide 116: SK Hynix Accelerator-in-Memory (2022)
https://news.skhynix.com/sk-hynix-develops-pim-next-generation-ai-accelerator/

## Slide 117: AliBaba PIM Recommendation System (2022)

## Slide 118: Eliminating the Adoption Barriers
Processing-in-Memory
in the Real World

## Slide 119: PIM Course (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream:
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 120: Processing in Memory: Two Approaches
1. Processing near Memory
2. Processing using Memory

## Slide 121: Eliminating the Adoption Barriers
How to Enable Adoption of Processing in Memory

## Slide 122: Potential Barriers to Adoption of PIM
1. Applications & software for PIM
2. Ease of programming (interfaces and compiler/HW support)
3. System and security support: coherence, synchronization, virtual memory, isolation, communication interfaces, …
4. Runtime and compilation systems for adaptive scheduling, data mapping, access/sharing control, …
5. Infrastructures to assess benefits and feasibility
All can be solved with change of mindset

## Slide 123: We Need to Revisit the Entire Stack
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
We can get there step by step

## Slide 124: Challenge and Opportunity for Future
Fundamentally
Energy-Efficient
(Data-Centric)
Computing Architectures

## Slide 125: Challenge and Opportunity for Future
Fundamentally
High-Performance
(Data-Centric)
Computing Architectures

## Slide 126: Challenge and Opportunity for Future
Computing Architectures
with
Minimal Data Movement

## Slide 127: Concluding Remarks
We must design systems to be balanced, high-performance, energy-efficient (all at the same time)  intelligent systems
  Data-centric, data-driven, data-aware
Enable computation capability inside and close to memory
This can
  Lead to orders-of-magnitude improvements
  Enable new applications & computing platforms
  Enable better understanding of nature
  …
Future of truly memory-centric computing is bright
  We need to do research & design across the computing stack
Notes: Perhaps we have taken processor-centric system design a bit too far

## Slide 128: Fundamentally Better Architectures
Data-centric
Data-driven
Data-aware

## Slide 129
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 130: Funding Acknowledgments
Alibaba, AMD, ASML, Google, Facebook, Hi-Silicon, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware, Xilinx
NSF
NIH
GSRC
SRC
CyLab
EFCL
Thank you!

## Slide 131: Acknowledgments
Think BIG, Aim HIGH!
https://safari.ethz.ch

## Slide 132
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 133: SAFARI Newsletter December 2021 Edition
https://safari.ethz.ch/safari-newsletter-december-2021/

## Slide 134: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 135: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 136: Special Research Sessions & Courses
Special Session at ISVLSI 2022: 9 cutting-edge talks
https://www.youtube.com/watch?v=qeukNs5XI3g

## Slide 137: Comp Arch (Fall 2021)
Fall 2021 Edition:
  https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Fall 2020 Edition:
  https://safari.ethz.ch/architecture/fall2020/doku.php?id=schedule
Youtube Livestream (2021):
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Youtube Livestream (2020):
  https://www.youtube.com/watch?v=c3mPdZA-Fmc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 138: DDCA (Spring 2022)
https://www.youtube.com/onurmutlulectures
Spring 2022 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2022/doku.php?id=schedule
Spring 2021 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2021/doku.php?id=schedule
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=cpXdE3HwvK0&list=PL5Q2soXY2Zi97Ya5DEUpMpO2bbAoaG7c6
Youtube Livestream (Spring 2021):
  https://www.youtube.com/watch?v=LbC0EZY8yw4&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN
Bachelor’s course
  2nd semester at ETH Zurich
  Rigorous introduction into “How Computers Work”
  Digital Design/Logic
  Computer Architecture
  10 FPGA Lab Assignments

## Slide 139: PIM Course (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream:
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 140: Genomics (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=bioinformatics
Youtube Livestream:
  https://www.youtube.com/watch?v=DEL_5A_Y3TI&list=PL5Q2soXY2Zi8NrPDgOR1yRU_Cxxjw-u18
Project course
  Taken by Bachelor’s/Master’s students
  Genomics lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 141: Hetero. Systems (Spring’22)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=heterogeneous_systems
Youtube Livestream:
  https://www.youtube.com/watch?v=oFO5fTrgFIY&list=PL5Q2soXY2Zi9XrgXR38IM_FTjmY6h7Gzm
Project course
  Taken by Bachelor’s/Master’s students
  GPU and Parallelism lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 142: HW/SW Co-Design (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=hw_sw_codesign
Youtube Livestream:
  https://youtube.com/playlist?list=PL5Q2soXY2Zi8nH7un3ghD2nutKWWDk-NK
Project course
  Taken by Bachelor’s/Master’s students
  HW/SW co-design lectures
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 143: Solid-State Drives (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=modern_ssds
Youtube Livestream:
  https://www.youtube.com/watch?v=_q4rm71DsY4&list=PL5Q2soXY2Zi8vabcse1kL22DEcgMl2RAq
Project course
  Taken by Bachelor’s/Master’s students
  SSD Basics and Advanced Topics
  Hands-on research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 144: RowHammer & DRAM Exploration (Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=softmc
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=softmc
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=r5QxuoJWttg&list=PL5Q2soXY2Zi_1trfCckr6PTN8WR72icUO
Bachelor’s course
  Elective at ETH Zurich
  Introduction to DRAM organization & operation
  Tutorial on using FPGA-based infrastructure
  Verilog & C++
  Potential research exploration

## Slide 145: Exploration of Emerging Memory Systems (Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=ramulator
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=ramulator
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=aM-llXRQd3s&list=PL5Q2soXY2Zi_TlmLGw_Z8hBo2925ZApqV
Bachelor’s course
  Elective at ETH Zurich
  Introduction to memory system simulation
  Tutorial on using Ramulator
  C++
  Potential research exploration

## Slide 146: Intelligent Architectures for Intelligent Machines
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
1 October 2022
INSAIT Conference

## Slide 147: Processing Using Memory: Extra Slides

## Slide 148: Mindset: Memory as an Accelerator
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 149: Starting Simple: Data Copy and Initialization
Forking
000000000000000
Zero initialization
(e.g., security)
VM Cloning
Deduplication
Checkpointing
Page Migration
Many more
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]

## Slide 150: Future Systems: In-Memory Copy
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
 90ns, 0.04uJ

## Slide 151: RowClone: In-DRAM Row Copy
Row Buffer (4 Kbytes)
Data Bus
8 bits
DRAM subarray
4 Kbytes
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
Negligible HW cost
Idea: Two consecutive ACTivates
Notes: copy

## Slide 152: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 153: More on RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Michael A. Kozuch, Phillip B. Gibbons, and Todd C. Mowry, "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization" Proceedings of the 46th International Symposium on Microarchitecture (MICRO), Davis, CA, December 2013. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 154: RowClone in Off-the-Shelf DRAM Chips
Idea: Violate DRAM timing parameters to mimic RowClone
https://parallel.princeton.edu/papers/micro19-gao.pdf

## Slide 155: Real Processing Using Memory Prototype
End-to-end RowClone & TRNG using off-the-shelf DRAM chips
Idea: Violate DRAM timing parameters to mimic RowClone
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 156: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s
Host Machine
FPGA Board
RISC-V System
PiM-Enabled DIMM

## Slide 157: Real Processing Using Memory Prototype
https://arxiv.org/pdf/2111.00082.pdf
https://github.com/cmu-safari/pidram
https://www.youtube.com/watch?v=qeukNs5XI3g&t=4192s

## Slide 158: Microbenchmark Copy/Initialization Throughput
In-DRAM Copy and Initialization improve throughput by 119x and 89x
Notes: This plot shows the throughput improvement provided by in-DRAM copy operations for bulk data initialization and copy over CPU-based copy and initialization using LOAD and STORE instructions. We do not execute any CLFLUSH instructions and assume that the data is up to date in DRAM and there are no cached copies.
The x-axis shows the size of the arrays that we copy or initialize. The dark gray bar shows the improvement for initialization operations, and the bright gray bar shows the improvement for copy operations.
[CLICK] We observe that in-DRAM copy and initialization operations improve copy and initialization throughput by 119x and 89x including the overheads of system support required for RowClone operations

## Slide 159: PiDRAM is Open Source
https://github.com/CMU-SAFARI/PiDRAM
Notes: PiDRAM is openly and freely available on Github. If you are interested in PiDRAM, please use it and feel free to contribute to it.

## Slide 160: Extended Version on ArXiv
https://arxiv.org/abs/2111.00082
Notes: An extended version of our conference paper is available on arXiv on this link where we discuss our framework in more detail.

## Slide 161: Long Talk + Tutorial on Youtube
https://youtu.be/s_z_S6FYpC8
Notes: I also describe PiDRAM in more detail and give a tutorial on how to use our framework in this SAFARI live seminar talk.

## Slide 162: (Truly) In-Memory Computation
We can support in-DRAM AND, OR, NOT, MAJ
At low cost
Using analog computation capability of DRAM
  Idea: activating multiple rows performs computation
30-60X performance and energy improvement
  Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology,” MICRO 2017.
New memory technologies enable even more opportunities
  Memristors, resistive RAM, phase change mem, STT-MRAM, …
  Can operate on data with minimal movement

## Slide 163: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 164: Bulk Bitwise Operations in Workloads
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017

## Slide 165: In-DRAM Acceleration of Database Queries
Seshadri+, “Ambit: In-Memory Accelerator for Bulk Bitwise Operations using Commodity DRAM Technology,” MICRO 2017.
>4-12X Performance Improvement

## Slide 166: More on Ambit
Vivek Seshadri, Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, and Todd C. Mowry, "Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology" Proceedings of the 50th International Symposium on Microarchitecture (MICRO), Boston, MA, USA, October 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Poster (pptx) (pdf)]

## Slide 167: In-DRAM Bulk Bitwise Execution
Vivek Seshadri and Onur Mutlu, "In-DRAM Bulk Bitwise Execution Engine" Invited Book Chapter in Advances in Computers, to appear in 2020. [Preliminary arXiv version]

## Slide 168: SIMDRAM Framework
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 169: SIMDRAM Framework: Overview
SIMDRAM Output
Instruction result
in memory
Step 3: Execution according to Program
Memory Controller
User Input
SIMDRAM-enabled application
ACT/PRE
ACT/PRE
ACT/PRE
ACT/ACT/PRE
done
SIMDRAM Output
User Input
AND/OR/NOT logic
Desired operation
Main memory
ISA
bbop_new
New SIMDRAM
instruction
Step 2: Generate
sequence of
DRAM commands
foo () {
bbop_new
}
Control Unit
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE
ACT/PRE/PRE
done
MAJ
MAJ/NOT logic
Step 1: Generate
MAJ logic
Program
New SIMDRAM Program
Program

## Slide 170: SIMDRAM Key Results
Evaluated on:
  16 complex in-DRAM operations
  7 commonly-used real-world applications
SIMDRAM provides:
88× and 5.8× the throughput of a CPU and a high-end GPU, respectively, over 16 operations
257× and 31× the energy efficiency of a CPU and a high-end GPU, respectively, over 16 operations
21× and 2.1× the performance of a CPU an a high-end GPU, over seven real-world applications

## Slide 171: More on SIMDRAM
Nastaran Hajinazar, Geraldo F. Oliveira, Sven Gregorio, Joao Dinis Ferreira, Nika Mansouri Ghiasi, Minesh Patel, Mohammed Alser, Saugata Ghose, Juan Gomez-Luna, and Onur Mutlu, "SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM" Proceedings of the 26th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, March-April 2021. [2-page Extended Abstract] [Short Talk Slides (pptx) (pdf)] [Talk Slides (pptx) (pdf)] [Short Talk Video (5 mins)] [Full Talk Video (27 mins)]

## Slide 172: In-DRAM Physical Unclonable Functions
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture Video (28 minutes)]

## Slide 173: In-DRAM True Random Number Generation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019. [Slides (pptx) (pdf)] [Full Talk Video (21 minutes)] [Full Talk Lecture Video (27 minutes)] Top Picks Honorable Mention by IEEE Micro.

## Slide 174: In-DRAM True Random Number Generation
Ataberk Olgun, Minesh Patel, A. Giray Yaglikci, Haocong Luo, Jeremie S. Kim, F. Nisa Bostanci, Nandita Vijaykumar, Oguz Ergin, and Onur Mutlu, "QUAC-TRNG: High-Throughput True Random Number Generation Using Quadruple Row Activation in Commodity DRAM Chips" Proceedings of the 48th International Symposium on Computer Architecture (ISCA), Virtual, June 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [SAFARI Live Seminar Video (1 hr 26 mins)]

## Slide 175: In-DRAM True Random Number Generation
F. Nisa Bostanci, Ataberk Olgun, Lois Orosa, A. Giray Yaglikci, Jeremie S. Kim, Hasan Hassan, Oguz Ergin, and Onur Mutlu, "DR-STRaNGe: End-to-End System Design for DRAM-based True Random Number Generators" Proceedings of the 28th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, April 2022. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)]
https://arxiv.org/pdf/2201.01385.pdf

## Slide 176: In-Flash Bulk Bitwise Execution
To appear at MICRO 2022
https://arxiv.org/pdf/2209.05566.pdf

## Slide 177: In-DRAM Lookup-Table Based Execution
To appear at MICRO 2022
https://arxiv.org/pdf/2104.07699.pdf