## Slide 1: The Story of RowHammer, RowPress & Beyond Can We Be Free of Bitflips (Soon)?
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
26 June 2024
Jean-Claude Laprie Award Talk at DSN 2024

## Slide 2: First RowHammer Work [ISCA 2014]
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data] [Lecture Video (1 hr 49 mins), 25 September 2020] One of the 7 papers of 2012-2017 selected as Top Picks in Hardware and Embedded Security for IEEE TCAD (link). Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 3: How Reliable/Secure/Safe is This Bridge?
Source: http://www.technologystudent.com/struct1/tacom1.png

## Slide 4: Collapse of the “Galloping Gertie”
Source: AP
http://www.wsdot.wa.gov/tnbhistory/connections/connections3.htm

## Slide 5: How Safe & Secure Are These People?
Source: https://s-media-cache-ak0.pinimg.com/originals/48/09/54/4809543a9c7700246a0cf8acdae27abf.jpg
Safety is about preventing unforeseen consequences

## Slide 6: How Robust Are Our Platforms?
Source: https://taxistartup.com/wp-content/uploads/2015/03/UK-Self-Driving-Cars.jpg
Robustness is about preventing unforeseen consequences

## Slide 7: What Is RowHammer?
One can predictably induce bit flips in commodity DRAM chips
  All recent DRAM chips are fundamentally vulnerable
First example of how a simple hardware failure mechanism can create a widespread system security vulnerability

## Slide 8: An “Early” Position Paper [IMW’13]
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Proceedings of the 5th International Memory Workshop (IMW), Monterey, CA, May 2013. Slides (pptx) (pdf) EETimes Reprint
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 9: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 10: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale
http://in4.iue.tuwien.ac.at/pdfs/sispad2021/P03.pdf

## Slide 11: As Memory Scales, It Becomes Unreliable
Data from all of Facebook’s servers worldwide
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers,” DSN’15.
Intuition: quadratic increase in capacity

## Slide 12: Large-Scale Failure Analysis of DRAM Chips
Analysis and modeling of memory errors found in all of Facebook’s server fleet
Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, "Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field" Proceedings of the 45th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Rio de Janeiro, Brazil, June 2015. [Slides (pptx) (pdf)] [DRAM Error Model]

## Slide 13: Infrastructures to Understand Such Issues
  An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms (Liu et al., ISCA 2013)
  The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study
  (Khan et al., SIGMETRICS 2014)
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
  Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case (Lee et al., HPCA 2015)
  AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems (Qureshi et al., DSN 2015)

## Slide 14: Infrastructures to Understand Such Issues
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 15: SoftMC: Open Source DRAM Infrastructure
Hasan Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 16: SoftMC: Open Source DRAM Infrastructure
https://github.com/CMU-SAFARI/SoftMC
Hasan Hassan, Nandita Vijaykumar, Samira Khan, Saugata Ghose, Kevin Chang, Gennady Pekhimenko, Donghyuk Lee, Oguz Ergin, and Onur Mutlu, "SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies" Proceedings of the 23rd International Symposium on High-Performance Computer Architecture (HPCA), Austin, TX, USA, February 2017. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Full Talk Lecture (39 minutes)] [Source Code]

## Slide 17: DRAM Bender
https://github.com/CMU-SAFARI/DRAM-Bender
Ataberk Olgun, Hasan Hassan, A Giray Yağlıkçı, Yahya Can Tuğrul, Lois Orosa, Haocong Luo, Minesh Patel, Oğuz Ergin, and Onur Mutlu, "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), 2023. [Extended arXiv version] [DRAM Bender Source Code] [DRAM Bender Tutorial Video (43 minutes)]

## Slide 18: DRAM Bender: Prototypes
Five out of the box FPGA-based prototypes
https://github.com/CMU-SAFARI/DRAM-Bender

## Slide 19: Data Retention in Memory [Liu et al., ISCA 2013]
Retention Time Profile of DRAM looks like this:
Location dependent
Stored value pattern dependent
Time dependent
Liu+, “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 20: RAIDR: Heterogeneous Refresh [ISCA’12]
Jamie Liu, Ben Jaiyen, Richard Veras, and Onur Mutlu, "RAIDR: Retention-Aware Intelligent DRAM Refresh" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pdf) [Invited Retrospective at 50 Years of ISCA, 2023 (pdf)] Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 21: Analysis of Data Retention Failures [ISCA’13]
Jamie Liu, Ben Jaiyen, Yoongu Kim, Chris Wilkerson, and Onur Mutlu, "An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms" Proceedings of the 40th International Symposium on Computer Architecture (ISCA), Tel-Aviv, Israel, June 2013. Slides (ppt) Slides (pdf) [Invited Retrospective at 50 Years of ISCA, 2023 (pdf)] Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 22: Infrastructure for Testing NAND Flash Chips
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017,
PIEEE 2017, HPCA 2018, SIGMETRICS 2018]

## Slide 23: Analysis of NAND Flash Errors [DATE’12]
Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, "Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis" Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Dresden, Germany, March 2012. Slides (ppt)

## Slide 24: Analysis of NAND Flash Errors [ITJ’13]
Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, "Error Analysis and Retention-Aware Error Management for NAND Flash Memory" Intel Technology Journal (ITJ) Special Issue on Memory Resiliency, Vol. 17, No. 1, May 2013.

## Slide 25: Analysis of NAND Flash Errors [PIEEE’17]
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 26: A Curious Phenomenon

## Slide 27: Modern DRAM is Prone to Disturbance Errors
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Hammered Row
Repeatedly reading a row enough times (before memory gets refreshed) induces disturbance errors in adjacent rows in most real DRAM chips you can buy today
Opened
Closed
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 28: Most DRAM Modules Are Vulnerable
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)

## Slide 29: Recent DRAM Is More Vulnerable
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 30: Why Is This Happening?
DRAM cells are too close to each other!
  They are not electrically isolated from each other
Access to one cell affects the value in nearby cells
  due to electrical interference between
    the cells
    wires used for accessing the cells
  Also called cell-to-cell coupling/interference
Example: When we activate (apply high voltage) to a row, an adjacent row gets slightly activated as well
  Vulnerable cells in that slightly-activated row lose a little bit of charge
  If RowHammer happens enough times, charge in such cells gets drained

## Slide 31: Higher-Level Implications
This simple circuit level failure mechanism has enormous implications on upper layers of the transformation hierarchy
Microarchitecture
ISA (Architecture)
Program/Language
Algorithm
Problem
Logic
Devices
Runtime System
(VM, OS, MM)
Electrons
Microarchitecture
ISA
Program/Language
Algorithm
Problem
Runtime System
(VM, OS, MM)
User
Logic
Devices
Electrons

## Slide 32: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 33: A Simple Program Can Induce Many Errors
CPU
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Avoid cache hits
  Flush X from cache
Avoid row hits to X
  Read Y in another row
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 34: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 35: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 36: A Simple Program Can Induce Many Errors
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  Download from: https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 37: Observed Errors in Real Systems
A real robustness issue
(including reliability, security, safety)
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: When we executed the code on four different processors, all four of them yielded errors. Intel Haswell has the most errors, at 23 thousand, because it has the highest rate of accessing DRAM.
Later on, I’ll show that we can induce as many as ten million disturbance errors in a more controlled environment.
From this, we conclude that disturbance errors are a serious reliability issue.

## Slide 38: First Adopters: Memory Testing Software
PassMark Software, memtest86, since 2014
  https://www.memtest86.com/troubleshooting.htm#hammer

## Slide 39: First Adopters: Memory Testing Software
PassMark Software, memtest86, since 2014
  https://www.memtest86.com/troubleshooting.htm#hammer

## Slide 40: One Can Take Over an Otherwise-Secure System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)

## Slide 41: RowHammer Security Attack Example
“Rowhammer” is a problem with some recent DRAM devices in which repeatedly accessing a row of memory can cause bit flips in adjacent rows (Kim et al., ISCA 2014).
  Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
We tested a selection of laptops and found that a subset of them exhibited the problem.
We built two working privilege escalation exploits that use this effect.
  Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn+, 2015)
One exploit uses rowhammer-induced bit flips to gain kernel privileges on x86-64 Linux when run as an unprivileged userland process.
When run on a machine vulnerable to the rowhammer problem, the process was able to induce bit flips in page table entries (PTEs).
It was able to use this to gain write access to its own page table, and hence gain read-write access to all of physical memory.
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn & Dullien, 2015)

## Slide 42: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 43: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 44: More Security Implications (I)
Source: https://lab.dsst.io/32c3-slides/7197.html
Rowhammer.js: A Remote Software-Induced Fault Attack in JavaScript (DIMVA’16)
“We can gain unrestricted access to systems of website visitors.”

## Slide 45: More Security Implications (II)
Source: https://fossbytes.com/drammer-rowhammer-attack-android-root-devices/
Drammer: Deterministic Rowhammer Attacks on Mobile Platforms, CCS’16
  “Can gain control of a smart phone deterministically”

## Slide 46: More Security Implications (III)
Using an integrated GPU in a mobile system to remotely escalate privilege via the WebGL interface. IEEE S&P 2018

## Slide 47: More Security Implications (IV)
Rowhammer over RDMA (I) USENIX ATC 2018

## Slide 48: More Security Implications (V)
Rowhammer over RDMA (II)

## Slide 49: More Security Implications (VI)
IEEE S&P 2020

## Slide 50: More Security Implications (VII)
USENIX Security 2019

## Slide 51: More Security Implications (VIII)
USENIX Security 2020

## Slide 52: More Security Implications (VIII)
USENIX Security 2022
Google’s Half-Double RowHammer Attack
https://www.usenix.org/system/files/sec22-kogler-half-double.pdf

## Slide 53: More Security Implications?

## Slide 54: A RowHammer Survey Across the Stack
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version] [Slides from COSADE 2019 (pptx)] [Slides from VLSI-SOC 2020 (pptx) (pdf)] [Talk Video (1 hr 15 minutes, with Q&A)]

## Slide 55: A RowHammer Survey: Recent Update
Onur Mutlu, Ataberk Olgun, and A. Giray Yaglikci, "Fundamentally Understanding and Solving RowHammer" Invited Special Session Paper at the 28th Asia and South Pacific Design Automation Conference (ASP-DAC), Tokyo, Japan, January 2023. [arXiv version] [Slides (pptx) (pdf)] [Talk Video (26 minutes)]
https://arxiv.org/pdf/2211.07613.pdf

## Slide 56: A Short Retrospective @ 50 Years of ISCA
https://arxiv.org/pdf/2306.16093

## Slide 57: Understanding RowHammer

## Slide 58: First RowHammer Analysis [ISCA 2014]
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data] [Lecture Video (1 hr 49 mins), 25 September 2020] One of the 7 papers of 2012-2017 selected as Top Picks in Hardware and Embedded Security for IEEE TCAD (link). Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 59: RowHammer Infrastructure (2012-2014)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 60
Tested
DRAM
Modules
from
2008-2014
(129 total)

## Slide 61: RowHammer Characterization Results
Most Modules Are at Risk
Errors vs. Vintage
Error = Charge Loss
Adjacency: Aggressor & Victim
Sensitivity Studies
Other Results in Paper
Solution Space
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors, (Kim et al., ISCA 2014)
Notes: Now I will present the characterization results, one-by-one.
First, I show that most modules are at risk. Second, I show the number of errors in a module as a function of the manufacture date. Third, I show that the errors are symptomatic of charge loss. Fourth, I show that an aggressor induces errors in adjacent rows. Fifth, I show several sensitivity studies. And, finally, I briefly describe other results in the paper.

## Slide 62: ❶ Access Interval (Aggressor)
Note: For three modules with the most errors (only first bank)
Not Allowed
Less frequent accesses  Fewer errors
55ns
500ns
Notes: In this figure, the x-axis is the interval at which we access the aggressor. And the y-axis is the number of errors. To comply with the DRAM standard, we employ a default value of 55ns in our experiments. However, as we increase the access-interval, we see that the number of errors decreases. In particular, at 500ns, there are no errors for all three modules.
From this, we conclude that less frequent accesses induce fewer errors.

## Slide 63: ❷ Refresh Interval
Note: Using three modules with the most errors (only first bank)
More frequent refreshes  Fewer errors
~7x frequent
64ms
Notes: In this figure, the x-axis is the refresh-interval. And the y-axis is the number of errors. To comply with the DRAM standard, we employ a default value of 64ms in our experiments. However, as we decrease the refresh-interval, we see that the number of errors decreases. In particular, when the refresh is shortened by 7x, there are no errors for all three modules.
From this, we conclude that more frequent accesses induce fewer errors.

## Slide 64: ❸ Data Pattern
RowStripe
~RowStripe
111111
111111
111111
111111
000000
000000
000000
000000
000000
111111
000000
111111
111111
000000
111111
000000
Solid
~Solid
10x Errors
Errors affected by data stored in other cells
Notes: We tested the modules with four different data-patterns: Solid, inverse Solid, RowStripe, and inverse RowStripe. Solid and inverse Solid give us full coverage since each cell is tested with both 1s and 0s. And the same applies to RowStripe and its inverse.
However, we found that the rowstripe pattern had 10 times as more errors than the solid pattern. We also tested many other data-patterns, including random, but found RowStripe to induce the most errors.
Therefore, we conclude that errors are affected by data stored in other cells due to differences in coupling effects between the cells.

## Slide 65: 6. Other Key Observations [ISCA’14]
Victim Cells ≠ Retention-Weak Cells
  Almost no overlap between them
Errors are repeatable
  Across ten iterations of testing, >70% of victim cells had errors in every iteration
As many as 4 errors per cache-line
  Simple ECC (e.g., SECDED) cannot prevent all errors
Cells affected by two aggressors on either side
  Double sided hammering
Notes: First, we show that victim cells are not weak cells, which are cells that are inherently leaky. According to our experiments, we saw almost no overlap between them.
Second, we show that errors are not strongly affected by temperature. In all of the tests so far, we set the temperature to 50 degrees Celsius. But even when we changed the temperature by 20 degrees, the number of errors changed by less than 15 percent.
Third, we show that errors are repeatable. Across ten iterations of testing, more than 70% of victim cells had errors in every iteration.

## Slide 66: Major RowHammer Characteristics (2014)
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data] [Lecture Video (1 hr 49 mins), 25 September 2020] One of the 7 papers of 2012-2017 selected as Top Picks in Hardware and Embedded Security for IEEE TCAD (link). Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 67: RowHammer is Getting Much Worse (2020)
Jeremie S. Kim, Minesh Patel, A. Giray Yaglikci, Hasan Hassan, Roknoddin Azizi, Lois Orosa, and Onur Mutlu, "Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques" Proceedings of the 47th International Symposium on Computer Architecture (ISCA), Valencia, Spain, June 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 68: RowHammer Has Many Dimensions (2021)
Lois Orosa, Abdullah Giray Yaglikci, Haocong Luo, Ataberk Olgun, Jisung Park, Hasan Hassan, Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Lightning Talk Video (1.5 minutes)] [arXiv version]

## Slide 69: RowHammer vs. Wordline Voltage (2022)
A. Giray Yağlıkçı, Haocong Luo, Geraldo F. de Oliviera, Ataberk Olgun, Minesh Patel, Jisung Park, Hasan Hassan, Jeremie S. Kim, Lois Orosa, and Onur Mutlu, "Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices" Proceedings of the 52nd Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Baltimore, MD, USA, June 2022. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [arXiv version] [Talk Video (34 minutes, including Q&A)] [Lightning Talk Video (2 minutes)]

## Slide 70: RowHammer in HBM Chips (2023)
Ataberk Olgun, Majd Osserian, A. Giray Yağlıkçı, Yahya Can Tugrul, Haocong Luo, Steve Rhyner, Behzad Salami, Juan Gomez-Luna, and Onur Mutlu, "An Experimental Analysis of RowHammer in HBM2 DRAM Chips" Proceedings of the 53nd Annual IEEE/IFIP International Conference on Dependable Systems and Networks Disrupt Track (DSN Disrupt), Porto, Portugal, June 2023. [arXiv version] [Slides (pptx) (pdf)] [Talk Video (24 minutes, including Q&A)]
https://arxiv.org/pdf/2305.17918.pdf

## Slide 71: RowHammer in HBM Chips (2024)
Appears at DSN 2024
https://arxiv.org/pdf/2310.14665

## Slide 72: RowHammer Spatial Variation Analysis (2024)
Appears at HPCA 2024
https://arxiv.org/pdf/2402.18652

## Slide 73: RowHammer Solutions

## Slide 74: Two Types of RowHammer Solutions
Immediate
  To protect the vulnerable DRAM chips in the field
  Limited possibilities
Longer-term
  To protect future DRAM chips
  Wider range of protection mechanisms
Our ISCA 2014 paper proposes both types of solutions
  Seven solutions in total
  PARA proposed as best solution  already employed in the field

## Slide 75: RowHammer Solution Approaches
More robust DRAM chips and/or error-correcting codes
Increased refresh rate
Physical isolation
Reactive refresh
Proactive throttling
DRAM Bank
Aggressor Row
Victim Rows
Isolation Rows
Large-enough distance
DRAM Bank
Aggressor Row
Victim rows
Refresh
Victim Rows
Refresh
Rapidly activated (hammered)
Fewer activations possible
in a refresh interval
Fewer activations allowed for aggressive applications
Cost, Power, Performance, Complexity
Notes: There are four high-level RowHammer mitigation approaches.
[CLICK] The first approach is to increase refresh rate
[CLICK] which reduces the refresh window,
[CLICK] and thus the activation count that an attacker can reach in a refresh window.
[CLICK] The second approach is to physically isolate
[CLICK] potential victim rows with sensitive data
[CLICK] from aggressor rows that a potential attacker can hammer
[CLICK] by allocating isolation rows in between
such that the attacker cannot disturb sensitive data by performing RowHammer attack.
[CLICK] The third approach is reactive refresh.
[CLICK] In this approach, when an aggressor row is hammered
[CLICK] potential victim rows are refreshed to avoid bit-flips.
[CLICK] Finally the fourth approach suggests
[CLICK] throttling or slowing down memory accesses proactively such that no row’s activation rate can reach RowHammer threshold.

## Slide 76: Apple’s Security Patch for RowHammer
https://support.apple.com/en-gb/HT204934
HP, Lenovo, and many other vendors released similar patches

## Slide 77: Our First Solution to RowHammer
PARA: Probabilistic Adjacent Row Activation
Key Idea
  After closing a row, activate (i.e., refresh) its neighbors with a low probability: p = 0.005
Reliability Guarantee
  When p=0.005, errors in one year: 9.4×10-14
  By adjusting the value of p, we can vary the strength of protection against errors
Notes: We provide a more efficient solution, called PARA, which stands for probabilistic adjacent row activation.
The key idea is thus: after closing a row, we activate (i.e., refresh) one of its neighbors with a low probability, for example, p equal to 0.005.
PARA provides a strong reliability guarantee even under the worst-case access patterns to DRAM. When we set p to 0.005, the expected number of errors in one year is 9.4 times 10 to the negative 14. This probability is much lower the failure rate of other hardware components, for example, the hard-disk drive.
And by adjusting the value of p, PARA can provide an arbitrarily strong-degree of protection against errors.

## Slide 78: Advantages of PARA
PARA refreshes rows infrequently
  Low power
  Low performance-overhead
    Average slowdown: 0.20% (for 29 benchmarks)
    Maximum slowdown: 0.75%
PARA is stateless
  Low cost
  Low complexity
PARA is an effective and low-overhead solution to prevent disturbance errors
Notes: PARA has many advantages. Since it refreshes row infrequently, it has low power and low performance-overhead. Simulated across 29 benchmarks, we saw an average of only 0.2% slowdown and a maximum of only 0.75% slowdown.
In addition, due to its stateless nature, PARA has low cost and complexity.
Therefore, PARA is an effective and low-overhead solution to prevent disturbance errors.

## Slide 79: Requirements for PARA
If implemented in DRAM chip (done today)
  Enough slack in timing and refresh parameters
  Plenty of slack today:
    Lee et al., “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common Case,” HPCA 2015.
    Chang et al., “Understanding Latency Variation in Modern DRAM Chips,” SIGMETRICS 2016.
    Lee et al., “Design-Induced Latency Variation in Modern DRAM Chips,” SIGMETRICS 2017.
    Chang et al., “Understanding Reduced-Voltage Operation in Modern DRAM Devices,” SIGMETRICS 2017.
    Ghose et al., “What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study,” SIGMETRICS 2018.
    Kim et al., “Solar-DRAM: Reducing DRAM Access Latency by Exploiting the Variation in Local Bitlines,” ICCD 2018.
If implemented in memory controller (done in past)
  Need coordination between controller and DRAM
  Memory controller should know which rows are physically adjacent

## Slide 80: Probabilistic Activation in Real Life (I)
https://twitter.com/isislovecruft/status/1021939922754723841

## Slide 81: Probabilistic Activation in Real Life (II)
https://twitter.com/isislovecruft/status/1021939922754723841

## Slide 82: Seven RowHammer Solutions Proposed
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data] [Lecture Video (1 hr 49 mins), 25 September 2020] One of the 7 papers of 2012-2017 selected as Top Picks in Hardware and Embedded Security for IEEE TCAD (link). Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 83: A Takeaway
Main Memory Needs
Intelligent Controllers
for Security, Safety, Reliability, Scaling

## Slide 84: Aside: Intelligent Controller for NAND Flash
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017,
PIEEE 2017, HPCA 2018, SIGMETRICS 2018]

## Slide 85: Intelligent Flash Controllers [PIEEE’17]
https://arxiv.org/pdf/1706.08642
Proceedings of the IEEE, Sept. 2017

## Slide 86: RowHammer in 2020-2024

## Slide 87: Revisiting RowHammer

## Slide 88: RowHammer is Getting Much Worse
Jeremie S. Kim, Minesh Patel, A. Giray Yaglikci, Hasan Hassan, Roknoddin Azizi, Lois Orosa, and Onur Mutlu, "Revisiting RowHammer: An Experimental Analysis of Modern Devices and Mitigation Techniques" Proceedings of the 47th International Symposium on Computer Architecture (ISCA), Valencia, Spain, June 2020. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (20 minutes)] [Lightning Talk Video (3 minutes)]

## Slide 89: Key Takeaways from 1580 Chips
Newer DRAM chips are much more vulnerable to RowHammer (more bit flips, happening earlier)
There are new chips whose weakest cells fail after only 4800 hammers
Chips of newer DRAM technology nodes can exhibit RowHammer bit flips 1) in more rows and 2) farther away from the victim row.
Existing mitigation mechanisms are NOT effective at future technology nodes
Notes: To reiterate our three key takeaways from our experimental characterization, we find that
[CLICK] First, chips of newer DRAM technology nodes are more vulnerable to RowHammer
[CLICK] Second, there are chips today whose weakest cells fail after only 4800 hammers
[CLICK] Third, chips of newer DRAM technology nodes can exhibit RowHammer bit flips in more rows and farther away from the victim row
================

## Slide 90: 1580 DRAM Chips Tested
1580 total DRAM chips tested from 300 DRAM modules
Three major DRAM manufacturers {A, B, C}
Three DRAM types or standards {DDR3, DDR4, LPDDR4}
  LPDDR4 chips we test implement on-die ECC
Two technology nodes per DRAM type {old/new, 1x/1y}
  Categorized based on manufacturing date, datasheet publication date, purchase date, and characterization results
Type-node: configuration describing a chip’s type and technology node generation: DDR3-old/new, DDR4-old/new, LPDDR4-1x/1y
Notes: Here we show a table that lists all the DRAM chips that we test
[CLICK] We characterize over 1500 DRAM chips from 300 DRAM modules
[CLICK] spanning the three major DRAM manufacturers which we anonymize as A, B, and C
[CLICK] of three DRAM types or standards DDR3, DDR4, and LPDDR4. We note that LPDDR4 chips that we test implement on-die ECC.
[CLICK] We identify two technology nodes per DRAM type (old/new, 1x and 1y) , which we categorize based on manufacturing date, datasheet publication date, purchase date, and characterization results
[CLICK] we define the term type-node which refers to the configuration describing a chip’s type and technology node generation. Across the chips we characterize, we identify the 6 DRAM type-node configurations listed

## Slide 91: Mitigation Mechanism Evaluation
105
104
103
102
105
104
103
102
DDR3-old
DDR3-new
DDR4-old
LPDDR4-1x
DDR4-new
LPDDR4-1y
PARA
TWiCe-ideal
Ideal
Ideal mechanism is significantly better
than any existing mechanism for HCfirst < 1024
Significant opportunity for developing a RowHammer solution
with low performance overhead that supports low HCfirst
HCfirst (number of hammers required to induce first RowHammer bit flip)
Notes: We find that the ideal refresh-based mitigation mechanism is significantly better than any existing mechanism as HCFirst reduces below 1024 .
[CLICK] And this indicates significant opportunity for developing a RowHammer solution with low performance overhead that also scales to low HCFirst values

## Slide 92: Key Takeaways
RowHammer is a
technology scaling problem
Finding a good solution to RowHammer is difficult (and will become more so)

## Slide 93: Reported HCfirst Values (2012 – Now)
HCfirst : Number of hammer for the first bitflip
HCfirst = 1 (DRAM doomed?)
HCfirst = ∞ (all good)
DDR3 @ 139K
[Kim+, ISCA’14]
*Not shown: Significant variance in HCfirst across vendors and die variations
DDR3 @ 24K
[Kim+, ISCA’20]
DDR4 @ 10K
[Kim+, ISCA’20]
LPDDR4 @ 4.8K
[Kim+, ISCA’20]
HBM2 @ 14K
[Olgun+, DSN’24]

## Slide 94: TRRespass

## Slide 95: Industry-Adopted Solutions Do Not Work
Pietro Frigo, Emanuele Vannacci, Hasan Hassan, Victor van der Veen, Onur Mutlu, Cristiano Giuffrida, Herbert Bos, and Kaveh Razavi, "TRRespass: Exploiting the Many Sides of Target Row Refresh" Proceedings of the 41st IEEE Symposium on Security and Privacy (S&P), San Francisco, CA, USA, May 2020. [Slides (pptx) (pdf)] [Lecture Slides (pptx) (pdf)] [Talk Video (17 minutes)] [Lecture Video (59 minutes)] [Source Code] [Web Article] Best Paper Award. IEEE Micro Top Pick Honorable Mention. Pwnie Award 2020 for Most Innovative Research. Pwnie Awards 2020

## Slide 96: A Poor RowHammer Solution
https://www.reddit.com/r/CrappyDesign/comments/arw0q8/now_this_this_is_poor_fencing/

## Slide 97: TRRespass
First work to show that TRR-protected DRAM chips are vulnerable to RowHammer in the field
  Mitigations advertised as secure are not secure
Introduces the Many-sided RowHammer attack
  Idea: Hammer many rows to bypass TRR mitigations (e.g., by overflowing proprietary TRR tables that detect aggressor rows)
(Partially) reverse-engineers the TRR and pTRR mitigation mechanisms implemented in DRAM chips and memory controllers
Provides an automatic tool that can effectively create many-sided RowHammer attacks in DDR4 and LPDDR4(X) chips

## Slide 98: Example Many-Sided Hammering Patterns

## Slide 99: BitFlips vs. Number of Aggressor Rows

## Slide 100: TRRespass Vulnerable DRAM Modules

## Slide 101: TRRespass Vulnerable Mobile Phones

## Slide 102: TRRespass Key Takeaways
RowHammer is still
an open problem
Security by obscurity
is likely not a good solution

## Slide 103: Improvements in JEDEC (2020-2021)
https://www.jedec.org/standards-documents/docs/jep300-1
https://www.jedec.org/standards-documents/docs/jep301-1

## Slide 104: Improvements in JEDEC (2024)

## Slide 105: Uncovering TRR Almost Completely

## Slide 106: Industry-Adopted Solutions Are Very Poor
Hasan Hassan, Yahya Can Tugrul, Jeremie S. Kim, Victor van der Veen, Kaveh Razavi, and Onur Mutlu, "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (25 minutes)] [Lightning Talk Video (100 seconds)] [arXiv version]
https://github.com/CMU-SAFARI/U-TRR

## Slide 107: Key Takeaways
All 45 modules we test are vulnerable
99.9% of rows in a DRAM bank experience at least one RowHammer bit flip
ECC is ineffective: up to 7 RowHammer bit flips in an 8-byte dataword
Notes: In summary, we find that all 45 modules we test are vulnerable to our new RowHammer access patterns
[CLICK] almost all rows in a DRAM bank experience at least one RowHammer bit flip
[CLICK] a single 8-byte dataword experiences up to 7 Rowhammer bit flips, making ECC ineffective against our RowHammer access patterns.
[CLICK] Our paper has detailed descriptions and analyses of each of the 45 modules and we encourage you to read it and attend our full talk

## Slide 108: Google’s Half-Double RowHammer Attack (May 2021)
https://security.googleblog.com/2021/05/introducing-half-double-new-hammering.html

## Slide 109: Google’s Half-Double RowHammer Attack (May 2021)
Given three consecutive rows A, B, and C, we were able to attack C by directing a very large number of accesses to A, along with just a handful (~dozens) to B.
Based on our experiments, accesses to B have a non-linear gating effect, in which they appear to “transport” the Rowhammer effect of A onto C.
This is likely an indication that the electrical coupling responsible for Rowhammer is a property of distance, effectively becoming stronger and longer-ranged as cell geometries shrink down.
https://security.googleblog.com/2021/05/introducing-half-double-new-hammering.html

## Slide 110: Google’s Half-Double RowHammer Attack
Appears at USENIX Security 2022
https://www.usenix.org/system/files/sec22-kogler-half-double.pdf

## Slide 111: Microsoft’s MOESI-prime Work [ISCA’22]
Introduces coherence-induced hammering
Hammering in commodity workloads (non-malicious code)
https://www.kevinloughlin.org/moesi-prime.pdf

## Slide 112: BlockHammer Solution in 2021
A. Giray Yaglikci, Minesh Patel, Jeremie S. Kim, Roknoddin Azizi, Ataberk Olgun, Lois Orosa, Hasan Hassan, Jisung Park, Konstantinos Kanellopoulos, Taha Shahroodi, Saugata Ghose, and Onur Mutlu, "BlockHammer: Preventing RowHammer at Low Cost by Blacklisting Rapidly-Accessed DRAM Rows" Proceedings of the 27th International Symposium on High-Performance Computer Architecture (HPCA), Virtual, February-March 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Intel Hardware Security Academic Awards Short Talk Slides (pptx) (pdf)] [Talk Video (22 minutes)] [Short Talk Video (7 minutes)] [Intel Hardware Security Academic Awards Short Talk Video (2 minutes)] [BlockHammer Source Code] Intel Hardware Security Academic Award Finalist (one of 4 finalists out of 34 nominations)

## Slide 113: Two Key Challenges
Scalability
with worsening RowHammer vulnerability
1
Compatibility
with commodity DRAM chips
2
Compatibility
with commodity DRAM chips
2
Compatibility
with commodity DRAM chips
2
Notes: Unfortunately, existing mechanisms face two key challenges.
[CLICK] Let's begin with the scalability challenge.

## Slide 114
A RowHammer attack hammers Row A
BlockHammer detects a RowHammer attack using area-efficient Bloom filters
BlockHammer selectively throttles accesses from within the memory controller
Bit flips do not occur
BlockHammer can optionally inform the system software about the attack
Physical
Row Layout
Row A
BlockHammer is compatible with commodity DRAM chips
No need for proprietary info of or modifications to DRAM chips
BlockHammer: Practical Throttling-based Mechanism
https://github.com/CMU-SAFARI/BlockHammer
Notes: In contrast, BlockHammer does not need this information [CLICK]
It detects an attack using area-efficient Bloom filters [CLICK]
And selectively throttles the attack’s memory accesses from within the memory controller [CLICK]
Due to throttling, the row’s activation count cannot reach critical levels, and no bit flip occurs [CLICK]
BlockHammer can optionally inform the system software about the attack for higher-level countermeasures [CLICK]
BlockHammer achieves all of these without needing proprietary information of or modifications to commodity DRAM chips, thereby overcoming the compatibility challenge[CLICK]

## Slide 115: A Takeaway
Main Memory Needs
Intelligent Controllers
for Security, Safety, Reliability, Scaling

## Slide 116: RowHammer Solution Approaches
More robust DRAM chips and/or error-correcting codes
Increased refresh rate
Physical isolation
Reactive refresh
Proactive throttling
DRAM Bank
Aggressor Row
Victim Rows
Isolation Rows
Large-enough distance
DRAM Bank
Aggressor Row
Victim rows
Refresh
Victim Rows
Refresh
Rapidly activated (hammered)
Fewer activations possible
in a refresh interval
Fewer activations allowed for aggressive applications
Cost, Power, Performance, Complexity
Notes: There are four high-level RowHammer mitigation approaches.
[CLICK] The first approach is to increase refresh rate
[CLICK] which reduces the refresh window,
[CLICK] and thus the activation count that an attacker can reach in a refresh window.
[CLICK] The second approach is to physically isolate
[CLICK] potential victim rows with sensitive data
[CLICK] from aggressor rows that a potential attacker can hammer
[CLICK] by allocating isolation rows in between
such that the attacker cannot disturb sensitive data by performing RowHammer attack.
[CLICK] The third approach is reactive refresh.
[CLICK] In this approach, when an aggressor row is hammered
[CLICK] potential victim rows are refreshed to avoid bit-flips.
[CLICK] Finally the fourth approach suggests
[CLICK] throttling or slowing down memory accesses proactively such that no row’s activation rate can reach RowHammer threshold.

## Slide 117: RowHammer in 2023: SK Hynix

## Slide 118: Industry’s Current RowHammer Solutions (I)

## Slide 119: Industry’s Current RowHammer Solutions (II)

## Slide 120: RowHammer in 2023: Samsung
https://arxiv.org/pdf/2302.03591v1.pdf

## Slide 121: A Solution from Microsoft
https://stefan.t8k2.com/publications/dramsec/2021/panopticon.pdf

## Slide 122: Solutions in JEDEC (April 2024)

## Slide 123: Evaluation of Industry’s Recent Solutions
To appear at DRAMSec 2024

## Slide 124: Question
Are we now
RowHammer-free
in 2024 and Beyond?

## Slide 125: Are We Now RowHammer Free in 2023?
Appeared at ISCA in June 2023
https://arxiv.org/pdf/2306.17061.pdf
https://github.com/CMU-SAFARI/RowPress

## Slide 126: RowPress

## Slide 127: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023. IEEE Micro Top Pick in 2024.

## Slide 128: What is RowPress?
Keeping a DRAM row open for a long time causes bitflips in adjacent rows
These bitflips do NOT require many row activations
Only one activation is enough in some cases!
Notes: So, what is RowPress?
[Click]
RowPress is the read disturbance caused by keeping a DRAM row open for a long time, which induces bitflips in adjacent rows
[Click]
These bitflips do not require many row activations,
[Click]
and we find in some cases only one row activation is enough.
[Click]
Now, lets see how this is different from RowHammer

## Slide 129: RowPress vs. RowHammer
Instead of using a high activation count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
We observe bitflips even with ONLY ONE activation in extreme cases where the row stays open for 30ms
36ns, 47K activations to induce bitflips
7.8µs, only 5K activations to induce bitflips
☞ increase the time that the aggressor row stays open
Notes: Instead of a high activation count, RowPress increases the time the that aggressor stays open.
Doing disturbs adjacent rows enough to cause bitflips without a very high activation count.
We observe bitflips even with only one activation in extreme cases.

## Slide 130: Real DRAM Chip Characterization (I)
FPGA-Based DDR4 Testing Infrastructure
Based on SoftMC [Hassan+, HPCA’17] and DRAM Bender [Olgun+, TCAD’23]
Fine-grained control over DRAM commands, timings, and temperature
https://github.com/CMU-SAFARI/DRAM-Bender
Notes: We use a FPGA based DDR4 testing infrastructure to characterize RowPress

## Slide 131: Real DRAM Chip Characterization (II)
DRAM chips tested
164 DDR4 chips from all 3 major DRAM manufacturers
Covers different die densities and revisions
Notes: We test 164 DDR4 chips from all 3 major DRAM manufacturers, covering different die densities and revisions

## Slide 132: Major Takeaways from Real DRAM Chips
RowPress significantly amplifies DRAM’s vulnerability to read disturbance
RowPress has a different underlying error mechanism from RowHammer
Notes: Our characterization yields the following two key takeaways

## Slide 133: Key Characteristics of RowPress (I)
Amplifying Read Disturbance in DRAM
Reduces the minimum number of row activations needed to induce a bitflip (ACmin) by 1-2 orders of magnitude
In extreme cases, activating a row only once induces bitflips
Notes: RowPress amplifies read disturbance because
First, it reduces the minimum number of row activations needed to induce a bitflip by 1-2 orders of magnitude
Second, in extreme cases, activating a row only once induces bitflips

## Slide 134: Key Characteristics of RowPress (II)
Amplifying Read Disturbance in DRAM
Reduces the minimum number of row activations needed to induce a bitflip (ACmin) by 1-2 orders of magnitude
In extreme cases, activating a row only once induces bitflips
Gets worse as temperature increases
Different From RowHammer
Affects a different set of cells compared to RowHammer and retention failures
Behaves differently as access pattern and temperature changes compared to RowHammer
Notes: Third, it gets worse as temperature increases
RowPress is different from RowHamer because it affects a different set of cells and behaves differently as access pattern and temperature changes

## Slide 135: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023. IEEE Micro Top Pick in 2024.

## Slide 136: More to Come…

## Slide 137: Two Major Directions
Understanding Bitflips (Hardware errors in general)
  Many effects on bitflips still need to be rigorously examined
    Aging of DRAM Chips
    Environmental Conditions (e.g., Process, Voltage, Temperature)
    Memory Access Patterns
    Memory Controller & System Design Decisions
    …
Solving Bitflips (Hardware errors in general)
  Flexible and efficient solutions are necessary
    In-field patchable / reconfigurable / programmable solutions
  Co-architecting across the system stack/components is important
    To avoid performance and denial-of-service problems

## Slide 138: Combining RowHammer and RowPress
Appears at DSN Disrupt 2024
https://arxiv.org/pdf/2406.13080v2

## Slide 139: Better Communication Between DRAM & Controller
https://arxiv.org/pdf/2204.10378.pdf

## Slide 140: Better Partitioning of DRAM & Controller
https://arxiv.org/pdf/2207.13358.pdf

## Slide 141: ABACuS: Another Intelligent Memory Controller
Ataberk Olgun, Yahya Can Tugrul, Nisa Bostanci, Ismail Emir Yuksel, Haocong Luo, Steve Rhyner, Abdullah Giray Yaglikci, Geraldo F. Oliveira, and Onur Mutlu, "ABACuS: All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation" To appear in Proceedings of the 33rd USENIX Security Symposium (USENIX Security), Philadelphia, PA, USA, August 2024. [arXiv version] [ABACuS Source Code]
https://github.com/CMU-SAFARI/ABACuS

## Slide 142: CoMeT: Another Intelligent Memory Controller
Appears at HPCA 2024
https://arxiv.org/pdf/2402.18769
https://github.com/CMU-SAFARI/CoMeT

## Slide 143: SVaRD: Another Intelligent Memory Controller
Appears at HPCA 2024
https://arxiv.org/pdf/2402.18652

## Slide 144: RowHammer Defenses Can Cause Denial of Service
https://arxiv.org/pdf/2404.13477

## Slide 145: Industry’s Recent Solutions Are Vulnerable
To appear at DRAMSec 2024

## Slide 146: Some RowHammer Works in 2024 (I)

## Slide 147: Some RowHammer Works in 2024 (II)

## Slide 148: Future Memory Robustness Challenges

## Slide 149: Technology Scaling Worsens Vulnerability
DRAM cells become increasingly more vulnerable (to read disturbance)
Technology node scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
[Luo+, ISCA’23]
[Kim+, ISCA’20]
[Kim+, ISCA’14]
Notes: With technology node scaling, DRAM cells get smaller in size and closer to each other[CLICK]
Such that we observe significant reductions in the minimum hammer count to induce the first bitflip in the last decade [CLICK]
Thus DRAM cells become increasingly more vulnerable to read disturbance [CLICK]

## Slide 150: Future of Main Memory Robustness
DRAM is becoming less reliable  more vulnerable
Due to difficulties in DRAM scaling, other problems may also appear (or they may be going unnoticed)
Some errors may already be slipping into the field
  Read disturb errors (Rowhammer, RowPress)
  Retention errors
  Read errors, write errors
  …
These errors can also pose safety & security vulnerabilities

## Slide 151: Future of Main Memory Robustness
DRAM
Flash memory
Emerging Technologies
  Phase Change Memory
  STT-MRAM
  RRAM, memristors
  FeRAM
  …

## Slide 152
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Understand and Model with Experiments (DRAM)

## Slide 153: Understand and Model with Experiments (DRAM)
Five out of the box FPGA-based prototypes
https://github.com/CMU-SAFARI/DRAM-Bender

## Slide 154: Understand and Model with Experiments (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
1x-nm
NAND Flash
[DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015, JSAC 2016, HPCA 2017, DFRWS 2017,
PIEEE 2017, HPCA 2018, SIGMETRICS 2018]
Cai+, “Error Characterization, Mitigation, and Recovery in Flash Memory Based Solid State Drives,” Proc. IEEE 2017.

## Slide 155: Collapse of the “Galloping Gertie” (1940)
Source: AP
http://www.wsdot.wa.gov/tnbhistory/connections/connections3.htm

## Slide 156: Another Example (1994)
Source: By 최광모 - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=35197984

## Slide 157: Yet Another Example (2007)
Source: Morry Gash/AP,
https://www.npr.org/2017/08/01/540669701/10-years-after-bridge-collapse-america-is-still-crumbling?t=1535427165809

## Slide 158: A More Recent Example (2018)
Source: AFP / Valery HACHE, https://www.capitalfm.co.ke/news/2018/08/genoa-bridge-collapse-what-we-know/

## Slide 159: A Most Recent Example (2022)
https://www.post-gazette.com/local/city/2022/01/28/pittsburgh-bridge-collapse-forbes-braddock-avenue-point-breeze-squirrel-hill/stories/202201280075

## Slide 160: A Most Recent Example (2022)
https://www.reuters.com/world/us/biden-highlight-manufacturing-jobs-gdp-growth-pittsburgh-2022-01-28/

## Slide 161: A Most Recent Example (2022)
https://usa.streetsblog.org/2022/01/28/pittsburgh-bridge-collapse-underscores-urgent-need-for-fix-it-first-policy/

## Slide 162: A Most Recent Example (2022)
https://www.npr.org/2022/01/28/1076343656/pittsburgh-bridge-collapse-biden-visit

## Slide 163: The Takeaway, Again
Intelligent Memory Controllers
Can Avoid Such Failures

## Slide 164: A Takeaway
Main Memory Needs
Intelligent Controllers
for Security, Safety, Reliability, Scaling

## Slide 165: Challenge and Opportunity for Future
Fundamentally
Robust
(Reliable, Secure, Safe)
Memory Systems

## Slide 166: Final Thoughts on RowHammer

## Slide 167: Before RowHammer (I)
https://www.cs.princeton.edu/~appel/papers/memerr.pdf
IEEE S&P 2003

## Slide 168: Before RowHammer (II)
https://www.cs.princeton.edu/~appel/papers/memerr.pdf
IEEE S&P 2003

## Slide 169: After RowHammer
A simple, exploitable memory error
can be induced by software

## Slide 170: After RowHammer
A simple, exploitable memory error
can be induced by software

## Slide 171: Perhaps Most Importantly…
RowHammer enabled a shift of mindset in mainstream security researchers
  General-purpose hardware is fallible, in a widespread manner
  Its problems are exploitable
This mindset has enabled many systems security researchers to examine hardware in more depth
  And understand HW’s inner workings and vulnerabilities
It is no coincidence that two of the groups that discovered Meltdown and Spectre heavily worked on RowHammer attacks before
  More to come…

## Slide 172: Conclusion

## Slide 173: Summary: RowHammer
Memory reliability is reducing
Reliability issues open up safety and vulnerabilities
  Very hard to defend against
Rowhammer is a prime example
  First example of how a simple hardware failure mechanism can create a widespread system security vulnerability
  Implications on system security & safety are tremendous & exciting
Bad news: RowHammer is getting worse
Good news: We have a lot more to do
  We are now fully aware hardware is easily fallible
  We are developing both attacks and defenses
  We are developing principled models, methodologies, solutions

## Slide 174: Acknowledgments
Think BIG, Aim HIGH!
https://safari.ethz.ch

## Slide 175
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 176: SAFARI Newsletter June 2023 Edition
https://safari.ethz.ch/safari-newsletter-june-2023/

## Slide 177: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 178: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 179
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 180: The Story of RowHammer, RowPress & Beyond Can We Be Free of Bitflips (Soon)?
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
26 June 2024
Jean-Claude Laprie Award Talk at DSN 2024

## Slide 181: RowHammer: Retrospective
New mindset that has enabled a renewed interest in HW security attack research:
  Real (memory) chips are vulnerable, in a simple and widespread manner  this causes real security problems
  Hardware reliability  security connection is now mainstream discourse
Many new RowHammer & bitflip attacks…
  Tens of papers in top security, architecture, systems venues
  More to come as RowHammer is getting worse (DDR4 & beyond)
Many new RowHammer solutions…
  Apple security release; Memtest86 updated
  Many solution proposals in top venues (latest in HPCA/Usenix Sec 2024)
  Principled system-DRAM co-design (in original RowHammer paper)
  More to come…

## Slide 182: DRAM Read Disturbance: A Critical Challenge
DRAM cells become increasingly more vulnerable to read disturbance
Technology node scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2023 | 1
2020 | 9.6
2014 | 139.2
[Luo+, ISCA’23]
[Kim+, ISCA’20]
[Kim+, ISCA’14]
Notes: With technology node scaling, DRAM cells get smaller in size and closer to each other[CLICK]
Such that we observe significant reductions in the minimum hammer count to induce the first bitflip in the last decade [CLICK]
Thus DRAM cells become increasingly more vulnerable to read disturbance [CLICK]

## Slide 183: Publicly-available RowHammer HCfirst Values
HCfirst Scale*
HCfirst = 1 (DRAM is doomed)
HCfirst = ∞ (all good)
DDR3-old @ 139K
[Kim+, ISCA’14]
*Not shown: Significant variance in HCfirst across vendors and die variations
DDR3-new @ 24K
[Kim+, ISCA’20]
DDR4-new @ 10K
[Kim+, ISCA’20]
LPDDR4-1y @ 4.8K
[Kim+, ISCA’20]
HBM2-20nm @ 14K
[Olgun+, DSN’24]
DDR3-old: manufactured before 2014 DDR3-new: manufactured in and after 2014
HBM-20nm: (likely) manufactured in 2018
DDR4-new: manufactured in and after 2016

## Slide 184: RowPress at tAggON = Refresh Interval
HCfirst Scale*
HCfirst = 1 (DRAM is doomed)
HCfirst = ∞ (all good)
*Not shown: Significant variance in HCfirst across vendors and die variations
row on time = 3.9 us
HBM2-20nm @ 335
[Olgun+, DSN’24]
row on time = 7.2 us
DDR4-new @ 380
[Luo+, ISCA’23]

## Slide 185: RowPress at tAggON = 9 * Refresh Interval
HCfirst Scale*
HCfirst = 1 (DRAM is doomed)
HCfirst = ∞ (all good)
*Not shown: Significant variance in HCfirst across vendors and die variations
row on time = 70.2 us
DDR4-new @ 51
[Luo+, ISCA’23]
row on time = 35.1 us
HBM2-20nm @ 123
[Olgun+, DSN’24]

## Slide 186: DRAM Array Layout
Wordline
Bitline
Active Region
Storage Node (SN)
Bitline
Contact
Cell
Top View
Capacitor
WL
Channel
Cross Section
P-Well
n+
Cell
BL
SN

## Slide 187: Mechanism 0: Reflecting Electric Field
P-Well
WL
BL
P-Well
N-Substrate

## Slide 188: Mechanism 1: Electron Injection
Precharge
P-Well
WL
Recombination
BL
A
V
e-
e-
e-
e-
e-
e-
e-
e-
e+
e-
P-Well
WL
Aggressor ACT
BL
e-
e-
e-
e-
e-
e-
e-

## Slide 189: Mechanism 2: Electron Drift
P-Well
WL
Aggressor ACT
BL
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
P-Well
WL
Electron Drift
BL
A
V
e-
e-
e-
e-
e-
e-
e-
e-
e+
e-

## Slide 190: More
Charge traps
Wordline Crosstalk

## Slide 191: BreakHammer
Key Observation: Mitigating DRAM read disturbance causes delays in memory accesses
Our Exploit: Denial of memory service is possible via triggering mitigation mechanisms
Key Idea: Throttling memory accesses of threads that trigger mitigation mechanisms repeatedly
BreakHammer:
  Detects the threads that repeatedly trigger the mitigation mechanisms
  Limits their on-the-fly memory request counts and MSHRs
  Near-zero area overhead and no additional memory access latency
Evaluation:
  Improves system performance by 48.7% on average (105.5% max)
  Reduces the maximum slowdown by 14.6% on average
Oğuzhan Canpolat, A. Giray Yağlıkçı, Ataberk Olgun, İsmail Emir Yüksel, Yahya Can Tuğrul, Konstantinos Kanellopoulos, Oğuz Ergin, Onur Mutlu, "Leveraging Adversarial Detection to Enable Scalable and Low Overhead RowHammer Mitigations,” [cs.CR] 2404.13477, 2024.
Notes: In summary,
[CLICK] The three major DRAM maintenance operations are refresh, RowHammer protection, and memory scrubbing.
[CLICK] We observe that implementing new and efficient maintenance mechanisms often requires difficult-to-realize changes in various system components, including the DRAM interface and the memory controller.
[CLICK] In this work, our goal is to first, ease the process of enabling new DRAM maintenance operations in DRAM and
[CLICK] enable more efficient in-DRAM maintenance operations
[CLICK] To this end, we propose Self-Managing DRAM (or SMD for short), which enables implementing new in-DRAM maintenance mechanisms with no further changes in the DRAM interface and the memory controller
[CLICK] According to our evaluations, SMD-based maintenance mechanisms achieve significant performance and energy efficiency benefits across many system configurations and workloads.
[CLICK] We release the source code of SMD on github.

## Slide 192: 3. Hammer Count (HC) Effects
RowHammer bit flip rates (i.e., RowHammer vulnerability)
increase with technology node generation
RowHammer bit flip rates increase
when going from old to new DDR4 technology node generations
Notes: We plot each of these curves across our DRAM type-node configurations per manufacturer
[CLICK] We find that newer DDR4 DRAM technology nodes show a clear trend of increasing RowHammer bit flip rates.
the same Hammer count value causes an increased RowHammer bit flip rate from DDR4-old to DDR4-new DRAM chips of all DRAM manufacturers
[CLICK] This indicates that RowHammer bit flip rates are increasing with newer technology node generations.
=======
spend more time.
Stronger second conclusion. Clear from this that rh bit flips increase with technology node generation. and we show DDR4 as an example.
rowhammer bit flip rates are increasing when going from old to new DDR4 technology nodes.

## Slide 193: TRRespass Key Results
13 out of 42 tested DDR4 DRAM modules are vulnerable
  From all 3 major manufacturers
  3-, 9-, 10-, 14-, 19-sided hammer attacks needed
5 out of 13 mobile phones tested vulnerable
  From 4 major manufacturers
  With LPDDR4(X) DRAM chips
These results are scratching the surface
  TRRespass tool is not exhaustive
  There is a lot of room for uncovering more vulnerable chips and phones

## Slide 194: TRRespass Based RowHammer Attack

## Slide 195: Architecting Robust Memory Systems
Understand: Methods for vulnerability modeling & discovery
  Modeling and prediction based on real (device) data and analysis
Architect: Principled architectures with security as key concern
  Good partitioning of duties across the stack
  Cannot give up performance and efficiency
  Patch-ability in the field
Design & Test: Principled design, automation, (online) testing
  Design for security/safety/reliability
  High coverage and good interaction with system reliability methods

## Slide 196: SAFARI Research Group: December 2021
https://safari.ethz.ch/safari-newsletter-december-2021/

## Slide 197
Think BIG, Aim HIGH!
https://www.youtube.com/watch?v=mV2OuB2djEs
SAFARI Introduction & Research
Computer architecture, HW/SW, systems, bioinformatics, security, memory

## Slide 198: Ramulator 2.0
Haocong Luo, Yahya Can Tugrul, F. Nisa Bostanci, Ataberk Olgun, A. Giray Yaglikci, and Onur Mutlu, "Ramulator 2.0: A Modern, Modular, and Extensible DRAM Simulator" Preprint on arxiv, August 2023. [arXiv version] [Ramulator 2.0 Source Code]
https://arxiv.org/pdf/2308.11030.pdf
https://github.com/CMU-SAFARI/ramulator2

## Slide 199: DRAM Bender
https://github.com/CMU-SAFARI/DRAM-Bender
Ataberk Olgun, Hasan Hassan, A Giray Yağlıkçı, Yahya Can Tuğrul, Lois Orosa, Haocong Luo, Minesh Patel, Oğuz Ergin, and Onur Mutlu, "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD), 2023. [Extended arXiv version] [DRAM Bender Source Code] [DRAM Bender Tutorial Video (43 minutes)]

## Slide 200: RowHammer & DRAM Exploration (Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=softmc
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=softmc
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=r5QxuoJWttg&list=PL5Q2soXY2Zi_1trfCckr6PTN8WR72icUO
Bachelor’s course
  Elective at ETH Zurich
  Introduction to DRAM organization & operation
  Tutorial on using FPGA-based infrastructure
  Verilog & C++
  Potential research exploration

## Slide 201: Exploration of Emerging Memory Systems (Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=ramulator
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=ramulator
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=aM-llXRQd3s&list=PL5Q2soXY2Zi_TlmLGw_Z8hBo2925ZApqV
Bachelor’s course
  Elective at ETH Zurich
  Introduction to memory system simulation
  Tutorial on using Ramulator
  C++
  Potential research exploration

## Slide 202: Overview of U-TRR
U-TRR: A new methodology to
uncover the inner workings of TRR
Key idea: Use data retention failures as a side channel
to detect when a row is refreshed by TRR
https://github.com/CMU-SAFARI/U-TRR
Notes: To this end, we propose U-TRR, a new methodology to uncover the inner workings of TRR.
[CLICK] The key idea of U-TRR is to use data retention failures in DRAM as a side channel to detect when a certain row is refreshed by TRR

## Slide 203: Bypassing ECC with New RowHammer Patterns
Conventional DRAM ECC cannot protect against our new RowHammer access patterns
Modules from all three vendors have many 8-byte data chunks with 3 and more (up to 7) RowHammer bit flips
Vendor A
Vendor B
Vendor C
https://github.com/CMU-SAFARI/U-TRR
Notes: The new RowHammer access patterns cause a lot of RowHammer bit flips. But can conventional DRAM ECC protect against those bit flips?
When we look at how RowHammer bit flips are distributed across 8-byte data chunks, we find that [CLICK] our RowHammer access patterns can cause at least 3 bit flips in modules of all three vendors. Further, [CLICK] we see up to 7 bit flips in many datawords, which the conventional SECDED ECC cannot correct or detect
[CLICK] We conclude that conventional DRAM ECC cannot protect against our new RowHammer patterns

## Slide 204: Initial RowHammer Studies

## Slide 205: 4. Adjacency: Aggressor & Victim
Most aggressors & victims are adjacent
Note: For three modules with the most errors (only first bank)
Adjacent
Adjacent
Adjacent
Non-Adjacent
Non-Adjacent
Notes: In this figure, the x-axis is the row-address difference between an aggressor and its victims. And the y-axis is the number of victim-aggressor pairs that correspond to the row-address difference. For all three modules, we see strong peaks at plus/minus 1. This implies that aggressors and victims have consecutive row-addresses, in other words, they are adjacent.
However, the figure also shows some victims that are not adjacent to the aggressor. We believe this could be caused by two reasons. First, depending on the mapping, two rows that are physically adjacent within the DRAM chip may not have consecutive row-addresses. Second, fault rows are often re-mapped to spare rows that may reside on a different portion of the DRAM chip.
Nevertheless, we conclude that the vast majority of aggressors & victims are adjacent.

## Slide 206: New RowHammer Characteristics

## Slide 207: RowHammer Has Many Dimensions
Lois Orosa, Abdullah Giray Yaglikci, Haocong Luo, Ataberk Olgun, Jisung Park, Hasan Hassan, Minesh Patel, Jeremie S. Kim, and Onur Mutlu, "A Deeper Look into RowHammer’s Sensitivities: Experimental Analysis of Real DRAM Chips and Implications on Future Attacks and Defenses" Proceedings of the 54th International Symposium on Microarchitecture (MICRO), Virtual, October 2021. [Slides (pptx) (pdf)] [Short Talk Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (21 minutes)] [Lightning Talk Video (1.5 minutes)] [arXiv version]

## Slide 208: Our Goal
Provide insights into three fundamental properties

Aggressor Row
Active Time

Victim DRAM Cell’s Physical Location
To find effective and efficient attacks and defenses
Notes: Our goal in this work is to Provide insights into three fundamental properties of RowHammer:
Temperature [CLICK]
Aggressor row active time [CLICK]
Victim DRAM cell's physical location [CLICK]
By doing so we aim enabling research to find effective and efficient attacks and defenses [CLICK]

## Slide 209: Summary of The Study & Key Results
272 DRAM chips from four major manufacturers
6 major takeaways from 16 novel observations
A RowHammer bit flip is more likely to occur
  in a bounded range of temperature
  if the aggressor row is active for longer time
  in certain physical regions of the DRAM module under attack
Our novel observations can inspire and aid future work
  Craft more effective attacks
  Design more effective and efficient defenses
Notes: Denser DRAM chips are more vulnerable to RowHammer [CLICK]
And Understanding RowHammer is critical to find effective and efficient solutions. However, no rigorous study demonstrates how this vulnerability varies under different conditions [CLICK]
In this work, our goal is to provide insights into three fundamental properties of RowHammer that can be leveraged to design more effective and efficient attacks and defenses These three properties are [CLICK]
DRAM chip temperature, [CLICK]
The time that an aggressor row stays active [CLICK]
and victim DRAM cell’s physical location [CLICK]
In this study, we test 272 real DRAM chips of DDR3 and DDR4 modules from four major manufacturers [CLICK]
Based on our analyses, we draw 6 key takeaway lessons from 16 novel observations. Among these, we highlight that [CLICK]
A RowHammer bit flip is more likely to occur [CLICK]
in a bounded range of temperature [CLICK]
if the aggressor row is active for longer time [CLICK]
And in certain physical regions of the DRAM module under attack [CLICK]
Based on our findings, we propose several improvements. We believe and hope that our novel observations will inspire and aid future work on crafting more effective attacks and designing more effective and efficient defense mechanisms [END]

## Slide 210
Reduces the minimum activation count to induce a bit flip by 36%
Bypasses defenses that do not account for this reduction
Time
Row A is active
Row B is active
Row A is active
Activating aggressor rows as frequently as possible:
Time
Row A is active
Row B is active
Keeping aggressor rows active for a longer time:
36% reduction in HCfirst
Example Attack Improvement 3: Bypassing Defenses with Aggressor Row Active Time
Notes: In the third example, an attacker can leverage the effect of aggressor row active time [CLICK]
In this scenario, instead of activating aggressor rows as frequently as possible, [CLICK]
the attacker can keep the aggressor rows active for longer time [CLICK]
Based on our analyses, HCfirst reduces by 36% on average with the proposed access pattern
With this reduction, an attacker can bypass RowHammer defenses that do not account for this reduction [CLICK]

## Slide 211: Example Defense Improvements
Example 1: Leveraging variation across DRAM rows
Example 2: Leveraging variation with temperature
  A DRAM cell experiences bit flips within a bounded temperature range
  A row can be disabled within the row’s vulnerable temperature range
Vulnerable Temperature Range
Temperature
no bit flips
no bit flips
Disable RowA
Temperature
Disable RowB
80% area reduction for Graphene [Park+, MICRO'20]
33% area reduction for BlockHammer [Yağlıkçı+, HPCA'21]
90%
10%
Breakdown of DRAM Rows
HCfirst
HCfirst
Aggressiveness can be reduced:
Notes: I will also explain two improvements for defense mechanisms in this slide, but you can find more in the paper [CLICK]
The first improvement leverages the variation across rows [CLICK]
We observe that 90% of the rows do not experience bit flips until the activation count reaches the double Hcfirst of the 10% of the rows.[CLICK]
Therefore, we can reduce the aggressiveness of defense mechanisms for 90% of the rows, which can reduce the area overheads of state-of-the-art defense mechanisms: [CLICK] BlockHammer and [CLICK] Graphene, by 33 and 80%, respectively [CLICK]
The second example leverages the variation in RowHammer vulnerability with temperature [CLICK]
We show that DRAM cells experience bit flips in bounded temperature ranges [CLICK]
To avoid bit flips, A DRAM row can be disabled when its cells are vulnerable to RowHammer at the current operating temperature [CLICK]

## Slide 212: Deeper Look into RowHammer: Talk Video
https://youtube.com/watch?v=fkM32oA0u6U&si=EnSIkaIECMiOmarE

## Slide 213: More RowHammer Analysis

## Slide 214: RowHammer vs. Wordline Voltage (2022)
A. Giray Yağlıkçı, Haocong Luo, Geraldo F. de Oliviera, Ataberk Olgun, Minesh Patel, Jisung Park, Hasan Hassan, Jeremie S. Kim, Lois Orosa, and Onur Mutlu, "Understanding RowHammer Under Reduced Wordline Voltage: An Experimental Study Using Real DRAM Devices" Proceedings of the 52nd Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Baltimore, MD, USA, June 2022. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [arXiv version] [Talk Video (34 minutes, including Q&A)] [Lightning Talk Video (2 minutes)]

## Slide 215: Updated DRAM Testing Infrastructure
  FPGA-based SoftMC (Xilinx Virtex UltraScale+ XCU200)
Fine-grained control over DRAM commands,
timing parameters (±1.5ns), temperature (±0.1°C ),
and wordline voltage (±1mV)
*Hassan et al., "SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies," in HPCA, 2017. [Available on GitHub: https://github.com/CMU-SAFARI/SoftMC]
*
Notes: We use an FPGA-based experimental setup programmed with a modified version of SoftMC [CLICK]
We control the chip temperature using a pair of heaters [CLICK] connected to a temperature controller [CLICK]
We supply the wordline voltage using the VPP power rail from an external power supply [CLICK]
This infrastructure provides fine-grained control over DRAM commands, timing parameters, temperature, and wordline voltage [CLICK]
=======

## Slide 216: Summary
Reducing wordline voltage can reduce RowHammer vulnerability without significantly affecting reliable DRAM operation
We provide the first RowHammer characterization under reduced wordline voltage
Experimental results with 272 real DRAM chips show that reducing wordline voltage:
Reduces RowHammer vulnerability
    Bit error rate caused by a RowHammer attack reduces by 15.2% (66.9% max)
    A row needs to be activated 7.4% more times (85.8% max) to induce the first bit flip
Increases row activation latency
    More than 76% of the tested DRAM chips reliably operate using nominal timing parameters
    Remaining 24% reliably operate with increased (up to 24ns) row activation latency
Reduces data retention time
    80% of the tested DRAM chips reliably operate using nominal refresh rate
    Remaining 20% reliably operate by
      Using single error correcting codes
      Doubling the refresh rate for a small fraction (16.4%) of DRAM rows
Notes: We provide the first RowHammer characterization using real DRAM chips under reduced wordline voltage [CLICK]
Our experimental results using 272 real DRAM chips show that with reduced wordline voltage, [CLICK]
RowHammer vulnerability reduces such that Bit flips occur at larger activation counts and fewer DRAM cells experience RowHammer bit flip [CLICK]
Reducing wordline voltage can increase row activation latency
  However, more than 75% of the tested DRAM chips reliably operate using nominal timing parameters
  And remaining 25% still reliably operate with increased row activation latency [CLICK]
Reducing wordline voltage can worsen data retention time
  However, 80% of the tested DRAM chips reliably operate using nominal refresh rate
  And remaining 20% experience bit flips that
    can be corrected using single error correcting codes
    or can be avoided by doubling the refresh rate for a small fraction (16.4%) of DRAM rows [CLICK]
Therefore we concluded that reducing wordline voltage can reduce RowHammer vulnerability without significantly affecting reliable DRAM operation [CLICK]

## Slide 217: RowHammer vs. Wordline Voltage: Talk Video
https://youtube.com/watch?v=fkM32oA0u6U&si=EnSIkaIECMiOmarE

## Slide 218: RowHammer in HBM Chips (2023)
Ataberk Olgun, Majd Osserian, A. Giray Yağlıkçı, Yahya Can Tugrul, Haocong Luo, Steve Rhyner, Behzad Salami, Juan Gomez-Luna, and Onur Mutlu, "An Experimental Analysis of RowHammer in HBM2 DRAM Chips" Proceedings of the 53nd Annual IEEE/IFIP International Conference on Dependable Systems and Networks Disrupt Track (DSN Disrupt), Porto, Portugal, June 2023. [arXiv version] [Slides (pptx) (pdf)] [Talk Video (24 minutes, including Q&A)]
https://arxiv.org/pdf/2305.17918.pdf

## Slide 219: RowHammer in HBM Chips (2024)
Appears at DSN 2024
https://arxiv.org/pdf/2310.14665

## Slide 220: RowHammer Spatial Variation Analysis (2024)
Appears at HPCA 2024
https://arxiv.org/pdf/2402.18652

## Slide 221: New RowHammer Solutions

## Slide 222: RowPress

## Slide 223: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023. IEEE Micro Top Pick in 2024.

## Slide 224: RowPress Amplifying Read Disturbance in Modern DRAM Chips
Haocong Luo
Ataberk Olgun A. Giray Yağlıkçı Yahya Can Tuğrul
Steve Rhyner Meryem Banu Cavlak Joël Lindegger
Mohammad Sadrosadati Onur Mutlu
ISCA 2023 Session 2B: Monday 19 June, 2:15 PM EDT
Notes: Hello, I am Haocong Luo. I will be presenting our work, RowPress, amplifying read disturbance in modern DRAM chips

## Slide 225: High-Level Summary
We demonstrate and analyze RowPress, a new read disturbance phenomenon that causes bitflips in real DRAM chips
We show that RowPress is different from the RowHammer vulnerability
We demonstrate RowPress using a user-level program on a real Intel system with real DRAM chips
We provide effective solutions to RowPress
Notes: In this work, we demonstrate and analyze RowPress, a new read disturbance phenomenon that causes bitflips in real DRAM chips
[Click]
We show that RowPress is different from RowHammer
[Click]
demonstrate RowPress in a real system with a user-level program
[Click]
And provide effective solutions to mitigate RowPress

## Slide 226: What is RowPress?
Keeping a DRAM row open for a long time causes bitflips in adjacent rows
These bitflips do NOT require many row activations
Only one activation is enough in some cases!
Now, let's delve into some background and
see how this is different from RowHammer
☞
Notes: So, what is RowPress?
[Click]
RowPress is the read disturbance caused by keeping a DRAM row open for a long time, which induces bitflips in adjacent rows
[Click]
These bitflips do not require many row activations,
[Click]
and we find in some cases only one row activation is enough.
[Click]
Now, lets see how this is different from RowHammer

## Slide 227: Are There Other Read-Disturb Issues in DRAM?
RowHammer is the only studied read-disturb phenomenon
Mitigations work by detecting high row activation count
What if there is another read-disturb phenomenon
that does NOT rely on high row activation count?
https://www.reddit.com/r/CrappyDesign/comments/arw0q8/now_this_this_is_poor_fencing/
Notes: RowHammer is the only studied read-disturb effect, and various mitigations work by detecting high row activation count.
This raises the following question, what if there is another read-disturb phenomenon that does not rely on high activation count?

## Slide 228: RowPress vs. RowHammer
Instead of using a high activation count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
We observe bitflips even with ONLY ONE activation in extreme cases where the row stays open for 30ms
36ns, 47K activations to induce bitflips
7.8µs, only 5K activations to induce bitflips
☞ increase the time that the aggressor row stays open
Notes: Instead of a high activation count, RowPress increases the time the that aggressor stays open.
Doing disturbs adjacent rows enough to cause bitflips without a very high activation count.
We observe bitflips even with only one activation in extreme cases.

## Slide 229: Real DRAM Chip Characterization (I)
FPGA-Based DDR4 Testing Infrastructure
Based on SoftMC [Hassan+, HPCA’17] and DRAM Bender [Olgun+, TCAD’23]
Fine-grained control over DRAM commands, timings, and temperature
https://github.com/CMU-SAFARI/DRAM-Bender
Notes: We use a FPGA based DDR4 testing infrastructure to characterize RowPress

## Slide 230: Real DRAM Chip Characterization (II)
DRAM chips tested
164 DDR4 chips from all 3 major DRAM manufacturers
Covers different die densities and revisions
Notes: We test 164 DDR4 chips from all 3 major DRAM manufacturers, covering different die densities and revisions

## Slide 231: Major Takeaways from Real DRAM Chips
RowPress significantly amplifies DRAM’s vulnerability to read disturbance
RowPress has a different underlying error mechanism from RowHammer
Notes: Our characterization yields the following two key takeaways

## Slide 232: Key Characteristics of RowPress (I)
Amplifying Read Disturbance in DRAM
Reduces the minimum number of row activations needed to induce a bitflip (ACmin) by 1-2 orders of magnitude
In extreme cases, activating a row only once induces bitflips
Notes: RowPress amplifies read disturbance because
First, it reduces the minimum number of row activations needed to induce a bitflip by 1-2 orders of magnitude
Second, in extreme cases, activating a row only once induces bitflips

## Slide 233: Key Characteristics of RowPress (II)
Amplifying Read Disturbance in DRAM
Reduces the minimum number of row activations needed to induce a bitflip (ACmin) by 1-2 orders of magnitude
In extreme cases, activating a row only once induces bitflips
Gets worse as temperature increases
Different From RowHammer
Affects a different set of cells compared to RowHammer and retention failures
Behaves differently as access pattern and temperature changes compared to RowHammer
Notes: Third, it gets worse as temperature increases
RowPress is different from RowHamer because it affects a different set of cells and behaves differently as access pattern and temperature changes

## Slide 234: Real-System Demonstration (I)
Key Idea: A proof-of-concept RowPress program keeps a DRAM row open for a longer period by keeping on accessing different cache blocks in the row
Intel Core i5-10400 (Comet Lake)
Samsung DDR4 Module M378A2K43CB1-CTD
(Date Code: 20-10)
w/ TRR RowHammer Mitigation
// Sync with Refresh and Loop Below
for (k = 0; k < NUM_AGGR_ACTS; k++)
for (j = 0; j < NUM_READS; j++) ∗AGGRESSOR1[j];
for (j = 0; j < NUM_READS; j++) ∗AGGRESSOR2[j];
for (j = 0; j < NUM_READS; j++)
clflushopt(AGGRESSOR1[j]);
clflushopt(AGGRESSOR2[j]);
mfence();
activate_dummy_rows();
Number of Cache Blocks Accessed
Per Aggressor Row ACT
(NUM_READS=1 is Rowhammer)
Notes: We demonstrate RowPress on a real system with a recent Intel processor and a Samsung DDR4 module with TRR rowhammer mitigation. The key idea of our RowPress program is to keep a DRAM row open for a longer period by keeping accessing different cache blocks in the row.
Here is the key part of our program, where we can change the number of cache blocks read per aggressor row activation. If we only read 1 cache block, then the program does the same as RowHammer

## Slide 235: Real-System Demonstration (II)
Leveraging RowPress, our user-level program
induces bitflips when RowHammer cannot
On 1500 victim rows
Notes: We run the program on 1500 arbitrarily selected victim rows, and we show the total number of bitflips we observe on the left, and the number of rows with bitflips on the right.
Leveraging RowPress, our program induces bitflips when RowHammer cannot

## Slide 236: Mitigating RowPress (I)
We propose a methodology to adapt existing RowHammer mitigations to also mitigate RowPress
Key Idea:
Limit the maximum row open time (tmro)
Configure the RowHammer mitigation to account for the RowPress-induced reduction in ACmin
Row Open Time
ACmin
RowPress-Induced
ACmin Reduction
Original
RowHammer
Mitigation
Adapted
Mitigation
tmro
Less
Row Buffer Locality
More RowPress Read Disturbance
Notes: We propose a methodology to adapt existing RH mitigations to also mitigate RowPress
They key idea is, based on characterization results, first limit the maximum row open time to strike a balance between row buffer locality and row press vulnerability, and then configure the RowHammer mitigation to account for the RowPress induced reduction in Acmin.
Our evaluation of the proposed methodology on two RowHammer mitigations, PARA and Graphene, shows that they can be adapted to also mitigate RowPress at low addition performance overhead.

## Slide 237: Mitigating RowPress (II)
Key evaluation results
Our solutions mitigate RowPress at low additional performance overhead
Chart: Additional Performance Overhead of Graphene-RP
| 36 | 66 | 96 | 186 | 336 | 636
Avg. Overhead | 0.013 | -0.0043 | -0.0063 | -0.0049 | -0.0014 | 0.006
Max Overhead | 0.102 | 0.066 | 0.064 | 0.05 | 0.05 | 0.046
Chart: Additional Performance Overhead of PARA-RP
| 36 | 66 | 96 | 186 | 336 | 636
Avg. Overhead | 0.032 | 0.036 | 0.045 | 0.06 | 0.079 | 0.129
Max Overhead | 0.238 | 0.134 | 0.131 | 0.147 | 0.194 | 0.316
Avg. -0.63%
Max. 6.4%
Avg. 4.5%
Max. 13.1%
Notes: Our evaluation results show that we can mitigate RowPress with low additional performance overhead

## Slide 238: More Results & Source Code
Many more results & analyses in the paper
6 major takeaways
19 major empirical observations
3 more potential mitigations
Fully open source and artifact evaluated
https://github.com/CMU-SAFARI/RowPress
https://arxiv.org/pdf/2306.17061.pdf
Notes: We have more results in the paper, and our work is fully open-source and artifact evaluated.

## Slide 239: RowPress [ISCA 2023]
Haocong Luo, Ataberk Olgun, Giray Yaglikci, Yahya Can Tugrul, Steve Rhyner, M. Banu Cavlak, Joel Lindegger, Mohammad Sadrosadati, and Onur Mutlu, "RowPress: Amplifying Read Disturbance in Modern DRAM Chips" Proceedings of the 50th International Symposium on Computer Architecture (ISCA), Orlando, FL, USA, June 2023. [Slides (pptx) (pdf)] [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (3 minutes)] [RowPress Source Code and Datasets (Officially Artifact Evaluated with All Badges)] Officially artifact evaluated as available, reusable and reproducible. Best artifact award at ISCA 2023. IEEE Micro Top Pick in 2024.

## Slide 240: More RowHammer in 2020-2024

## Slide 241: RowHammer in 2020 (I)

## Slide 242: RowHammer in 2020 (II)

## Slide 243: RowHammer in 2020 (III)

## Slide 244: RowHammer in 2020 (IV)
CHES 2020
An FPGA-based RowHammer attack recovering private keys twice as fast compared to CPU-based attacks

## Slide 245: RowHammer in 2021 (I)

## Slide 246: RowHammer in 2021 (II)

## Slide 247: RowHammer in 2021 (III)

## Slide 248: RowHammer in 2022 (I)

## Slide 249: RowHammer in 2022 (II)

## Slide 250: RowHammer in 2022 (III)

## Slide 251: RowHammer in 2022 (IV)

## Slide 252: RowHammer in 2022 (V)

## Slide 253: RowHammer in 2022 (VI)

## Slide 254: RowHammer in 2022 (VII)

## Slide 255: RowHammer in 2022 (VII)
A. Giray Yaglıkcı, Ataberk Olgun, Minesh Patel, Haocong Luo, Hasan Hassan, Lois Orosa, Oguz Ergin, and Onur Mutlu, "HiRA: Hidden Row Activation for Reducing Refresh Latency of Off-the-Shelf DRAM Chips" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, IL, USA, October 2022. [Slides (pptx) (pdf)] [Longer Lecture Slides (pptx) (pdf)] [Lecture Video (36 minutes)] [arXiv version]
https://arxiv.org/pdf/2209.10198.pdf

## Slide 256: RowHammer in 2022 (VIII)
https://arxiv.org/pdf/2204.10378.pdf

## Slide 257: RowHammer in 2022 (IX)
https://arxiv.org/pdf/2207.13358.pdf

## Slide 258: RowHammer in 2023 (I)

## Slide 259: RowHammer in 2023 (II)

## Slide 260: RowHammer in 2023 (III): SK Hynix

## Slide 261: Industry’s RowHammer Solutions (I)

## Slide 262: Industry’s RowHammer Solutions (II)

## Slide 263: RowHammer in 2023 (IV): Samsung
https://arxiv.org/pdf/2302.03591v1.pdf

## Slide 264: RowHammer in 2023 (V)

## Slide 265: RowHammer in 2023 (VI)
SOSP 2023

## Slide 266: RowHammer in 2023 (VII)
IEEE Computer Architecture Letters, 2023
IEEE Embedded Systems Letters, 2023

## Slide 267: Ramulator 2.0
"Ramulator 2.0: A Modern, Modular, and Extensible DRAM Simulator" IEEE Computer Architecture Letters, August 2023. (Preprint on arxiv) [arXiv version] [Ramulator 2.0 Source Code]

## Slide 268: RowHammer in 2023 (VIII)
MEMSYS 2023
MICRO 2023

## Slide 269: Self-Managing DRAM

## Slide 270: Self-Managing DRAM: Overview
Self-Managing DRAM (SMD)
enables autonomous in-DRAM maintenance operations
ACT_NACK pin
Memory Controller
DRAM Chip
command bus
data bus
Leveraging the ability to reject an ACT, a maintenance operation can be implemented completely within a DRAM chip
Key Idea:
Prevent the memory controller from accessing DRAM regions that are under maintenance by rejecting row activation (ACT) commands
Notes: We propose Self-Managing DRAM, or SMD for short.
[CLICK] The key idea of SMD is to prevent the memory controller from accessing DRAM regions that are under maintenance by rejecting row activation commands
[CLICK] To provide a DRAM chip with the ability to reject an activate command, SMD slightly extends the existing interface between the memory controller and the DRAM chips. [CLICK] SMD adds a single negative-acknowledgment (ACT_NACK) pin to a DRAM chip, which the chip uses to signal the memory controller that it rejects the latest activate command.
[CLICK] Leveraging SMD’s ability to reject an activate command, a maintenance operation can be implemented completely within a DRAM chip

## Slide 271: SMD-Based Maintenance Mechanisms
DRAM
Refresh
RowHammer Protection
Memory Scrubbing
Fixed Rate (SMD-FR)
Variable Rate (SMD-VR)
uniformly refreshes all DRAM rows with a fixed refresh period
skips refreshing rows that can retain their data for longer than the default refresh period
Probabilistic (SMD-PRP)
Deterministic (SMD-DRP)
keeps track of most frequently activated rows and performs neighbor row refresh when activation count threshold is exceeded
Periodic Scrubbing (SMD-MS)
periodically scans the entire DRAM for errors and corrects them
Performs neighbor row refresh with a small probability on every row activation
Notes: Using the Self-Managing DRAM architecture, we develop various maintenance mechanisms.
[CLICK] For DRAM refresh, [CLICK] we develop Fixed-Rate Refresh (SMD-FR), which uniformly refreshes all DRAM rows with a fixed refresh period.
[CLICK] Also, we develop Variable Rate Refresh (SMD-VR), which uses retention profiling information to skip refreshing rows that can retain their data correctly for extended periods.
[CLICK] For RowHammer Protection, [CLICK] we develop Probabilistic RowHammer Protection (SMD-PRP), which performs neighbor row refresh with a small probability on every row activation.
[CLICK] Second, we develop Deterministic RowHammer Protection (SMD-DRP), which identifies frequently activated rows and refreshes only their neighbor rows when needed.
[CLICK] Last, we develop a mechanism for memory scrubbing. [CLICK] SMD-MS periodically scans the entire DRAM for errors and corrects them.
Thanks to SMD, we all these mechanisms can be implemented completely within DRAM and they can operate together.

## Slide 272: Self-Managing DRAM: Summary
Implementing new maintenance mechanisms often requires difficult-to-realize changes
The three major DRAM maintenance operations:
  Refresh
  RowHammer Protection
  Memory Scrubbing
Our Goal
Ease the process of enabling new DRAM maintenance operations
1
Enable more efficient in-DRAM maintenance operations
2
Self-Managing DRAM (SMD)
Enables implementing new in-DRAM maintenance mechanisms with no further changes in the DRAM interface and memory controller
SMD-based refresh, RowHammer protection, and scrubbing achieve 9.2% speedup and 6.2% lower DRAM energy vs. conventional DRAM
Notes: In summary,
[CLICK] The three major DRAM maintenance operations are refresh, RowHammer protection, and memory scrubbing.
[CLICK] We observe that implementing new and efficient maintenance mechanisms often requires difficult-to-realize changes in various system components, including the DRAM interface and the memory controller.
[CLICK] In this work, our goal is to first, ease the process of enabling new DRAM maintenance operations in DRAM and
[CLICK] enable more efficient in-DRAM maintenance operations
[CLICK] To this end, we propose Self-Managing DRAM (or SMD for short), which enables implementing new in-DRAM maintenance mechanisms with no further changes in the DRAM interface and the memory controller
[CLICK] According to our evaluations, SMD-based maintenance mechanisms for refresh, RowHammer protection, and memory scrubbing achieve significant performance and energy efficiency benefits compared to conventional DDR4 DRAM.

## Slide 273: Talk on Self-Managing DRAM
https://www.youtube.com/watch?v=mGa6-vpExbE

## Slide 274: Related Courses

## Slide 275: DDCA (Spring 2022)
https://www.youtube.com/onurmutlulectures
Spring 2022 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2022/doku.php?id=schedule
Spring 2021 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2021/doku.php?id=schedule
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=cpXdE3HwvK0&list=PL5Q2soXY2Zi97Ya5DEUpMpO2bbAoaG7c6
Youtube Livestream (Spring 2021):
  https://www.youtube.com/watch?v=LbC0EZY8yw4&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN
Bachelor’s course
  2nd semester at ETH Zurich
  Rigorous introduction into “How Computers Work”
  Digital Design/Logic
  Computer Architecture
  10 FPGA Lab Assignments

## Slide 276: Comp Arch (Fall 2022)
Fall 2022 Edition:
  https://safari.ethz.ch/architecture/fall2022/doku.php?id=schedule
Fall 2021 Edition:
  https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Youtube Livestream (2022):
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Youtube Livestream (2021):
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 277: RowHammer & DRAM Exploration (Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=softmc
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=softmc
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=r5QxuoJWttg&list=PL5Q2soXY2Zi_1trfCckr6PTN8WR72icUO
Bachelor’s course
  Elective at ETH Zurich
  Introduction to DRAM organization & operation
  Tutorial on using FPGA-based infrastructure
  Verilog & C++
  Potential research exploration

## Slide 278: Exploration of Emerging Memory Systems (Fall 2022)
https://www.youtube.com/onurmutlulectures
Fall 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2022/doku.php?id=ramulator
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=ramulator
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=aM-llXRQd3s&list=PL5Q2soXY2Zi_TlmLGw_Z8hBo2925ZApqV
Bachelor’s course
  Elective at ETH Zurich
  Introduction to memory system simulation
  Tutorial on using Ramulator
  C++
  Potential research exploration

## Slide 279: An Early Proposal for Intelligent Controllers [IMW’13]
Onur Mutlu, "Memory Scaling: A Systems Architecture Perspective" Proceedings of the 5th International Memory Workshop (IMW), Monterey, CA, May 2013. Slides (pptx) (pdf) EETimes Reprint
https://people.inf.ethz.ch/omutlu/pub/memory-scaling_memcon13.pdf

## Slide 280: Industry Is Writing Papers About It, Too

## Slide 281: Industry Is Writing Papers About It, Too

## Slide 282: Final Thoughts on RowHammer

## Slide 283: Aside: Byzantine Failures
This class of failures is known as Byzantine failures
Characterized by
  Undetected erroneous computation
  Opposite of “fail fast (with an error or no result)”
“erroneous” can be “malicious” (intent is the only distinction)
Very difficult to detect and confine Byzantine failures
Do all you can to avoid them
Lamport et al., “The Byzantine Generals Problem,” ACM TOPLAS 1982.
Slide credit: Mahadev Satyanarayanan, CMU, 15-440, Spring 2015

## Slide 284: Aside: Byzantine Generals Problem
https://dl.acm.org/citation.cfm?id=357176
ACM TOPLAS 1982

## Slide 285: Funding Acknowledgments
Alibaba, AMD, ASML, Google, Facebook, Hi-Silicon, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware, Xilinx
Microsoft Swiss JRC
NSF
NIH
GSRC
SRC
CyLab
EFCL
Thank you!

## Slide 286: First RowHammer Analysis [ISCA 2014]
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)] [Source Code and Data] [Lecture Video (1 hr 49 mins), 25 September 2020] One of the 7 papers of 2012-2017 selected as Top Picks in Hardware and Embedded Security for IEEE TCAD (link). Selected to the ISCA-50 25-Year Retrospective Issue covering 1996-2020 in 2023 (Retrospective (pdf) Full Issue).

## Slide 287: Retrospective on RowHammer & Future
https://people.inf.ethz.ch/omutlu/pub/rowhammer-and-other-memory-issues_date17.pdf
Onur Mutlu, "The RowHammer Problem and Other Issues We May Face as Memory Becomes Denser" Invited Paper in Proceedings of the Design, Automation, and Test in Europe Conference (DATE), Lausanne, Switzerland, March 2017. [Slides (pptx) (pdf)]

## Slide 288: A More Recent RowHammer Retrospective
Onur Mutlu and Jeremie Kim, "RowHammer: A Retrospective" IEEE Transactions on Computer-Aided Design of Integrated Circuits and Systems (TCAD) Special Issue on Top Picks in Hardware and Embedded Security, 2019. [Preliminary arXiv version] [Slides from COSADE 2019 (pptx)] [Slides from VLSI-SOC 2020 (pptx) (pdf)] [Talk Video (1 hr 15 minutes, with Q&A)]

## Slide 289: A RowHammer Survey: Recent Update
Onur Mutlu, Ataberk Olgun, and A. Giray Yaglikci, "Fundamentally Understanding and Solving RowHammer" Invited Special Session Paper at the 28th Asia and South Pacific Design Automation Conference (ASP-DAC), Tokyo, Japan, January 2023. [arXiv version] [Slides (pptx) (pdf)] [Talk Video (26 minutes)]
https://arxiv.org/pdf/2211.07613.pdf

## Slide 290: RowHammer & RowPress on HBM Chips

## Slide 291: An Experimental Analysis of RowHammer in HBM2 DRAM Chips
Ataberk Olgun Majd Osseiran
A. Giray Yağlıkçı
Yahya Can Tuğrul
Steve Rhyner
Haocong Luo
Juan Gomez Luna
Onur Mutlu
Behzad Salami
Notes: Hello all,
I am Ataberk and I will present our work, An Experimental Analysis of RowHammer in HBM2 DRAM Chips

## Slide 292: The RowHammer Vulnerability (I)
CPU
DRAM Module
DRAM Chip
Notes: Let me first explain the RowHammer vulnerability
This is a typical DRAM-based computing sytem with a CPU and a DRAM module
[CLICK] We will look at a simplified depiction of this DRAM chip

## Slide 293: The RowHammer Vulnerability (II)
Row 0
Row 1
Row 2
Row 3
Row 4
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bit flips in nearby rows
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 2
closed
Victim Row
Victim Row
Victim Row
Victim Row
Aggressor Row
Row 2
open
Row 2
closed
Aggressor Row
DRAM Chip
Notes: This simple chip contains many DRAM rows.
In order to access data from a DRAM row, say row 2, the memory controller must first open or activate the row [CLICK].
After all requests are serviced from row 2, the memory controller must close or precharge the row [CLICK] in order to begin accessing data from another row.
[BACK & FORTH] Due to an increase in cell-to-cell interference, rapidly activating and precharging a DRAM row can result in bit flips in nearby rows [CLICK]
[FORTH & BACK] Continuing to access the same row results in even more failures in nearby rows. This phenomenon is known as RowHammer. [CLICK]
We refer to the rapidly accessed row as an aggressor row and the rows containing bit flips as victim rows.

## Slide 294: A Simple Program Can Induce Bitflips
CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  https://github.com/CMU-SAFARI/rowhammer
DRAM Module
Notes: A user-level program can induce RowHammer bitflips, in a similar way, in main memory by running this code on the bottom left.

## Slide 295: One Can Take Over a System
Exploiting the DRAM rowhammer bug to gain kernel privileges (Seaborn, 2015)
Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors (Kim et al., ISCA 2014)
Notes: Prior works, such as this one, shows that RowHammer is a widespread phenomenon affecting almost all types of DRAM chips from various manufacturers in the field.
[CLICK] RowHammer is a problem because the previous user-level program accesses one memory location and has unintended side effects on data stored in other addresses. In other words RowHammer breaks memory isolation.
Memory isolation is a key property of reliable and secure computing systems.
[CLICK] and many prior works including this one have shown that RowHammer can be used to take over systems.

## Slide 296: Most DRAM Modules Are Vulnerable (2020)
All tested DRAM types are susceptible to RowHammer bitflips
What about High Bandwidth Memory (HBM)?
Kim et al., ”Revisiting RowHammer: An Experimental Analysis of Modern DRAM Devices and Mitigation Techniques," in ISCA, 2020.
Notes: Many of the newer DRAM chips of different types are also vulnerable to RowHammer as demonstrated by a recent work.
[CLICK] Considering these recent developments in RowHammer, we ask the question, “what about new high bandwidth memory DRAM”? Does RowHammer exist in High Bandwidth Memory, and if so how does the RowHammer in real High Bandwidth Memory chips look like?

## Slide 297: Executive Summary
Motivation: HBM chips have new architectural characteristics (e.g., 3D-stacked dies) that might affect the RowHammer vulnerability in various ways
Understanding RowHammer enables designing effective and efficient solutions
Problem: No prior study demonstrates the RowHammer vulnerability in HBM
Goal: Experimentally analyze how vulnerable HBM DRAM chips are to RowHammer
Experimental Study: Detailed experimental characterization of RowHammer in a modern HBM2 DRAM chip. Our study provides two main findings:
1. Spatial variation of RowHammer vulnerability
Different channels in a 3D-stacked HBM chip exhibit different RowHammer vulnerability
DRAM rows near the end of a DRAM bank are more RowHammer resilient
2. On-DRAM-die RowHammer mitigations
A modern HBM chip implements undisclosed on-DRAM-die RowHammer mitigation
The mitigation refreshes a victim row after every 17 periodic refresh operations (e.g., similar to DDR4 chips)
Notes: HBM chips harbor new architectural characteristics that might affect the RowHammer vulnerability
[CLICK] Understanding RowHammer enables designing effective and efficient solutions
[CLICK] However, no rigorous study demonstrates the RowHammer vulnerability in HBM
[CLICK] Our goal is to experimentally analyze how vulnerable real HBM chips are to RowHammer
[CLICK] Therefore, we perform a detailed experimental characterization of RowHammer in a modern HBM2 DRAM chip and we provide two main findings.
[CLICK] First, we show that there is substantial variation in RowHammer vulnerability in different physical locations of high bandwidth memory chips. Different channels in 3D-stacked HBM chips exhibit different vulnerability, and
[CLICK] DRAM rows near the end of a DRAM bank are more RowHammer resilient
[CLICK] Second, we show that a modern HBM chip implements undisclosed on-DRAM-die Rowhammer mitigation
[CLICK] We find that this particular mitigation refreshes a victim row after every 17 periodic refresh operations, resembling a mitigation prior work found in DDR4 chips

## Slide 298: Outline
1. HBM DRAM Organization & Operation
2. DRAM Cell Leakage & RowHammer
4. RowHammer Spatial Variation Analysis
5. On-die RowHammer Mitigation Analysis
3. HBM DRAM Testing Methodology
6. Conclusion
Notes: Here is the outline of my talk.

## Slide 299: Outline
1. HBM DRAM Organization & Operation
2. DRAM Cell Leakage & RowHammer
4. RowHammer Spatial Variation Analysis
5. On-die RowHammer Mitigation Analysis
3. HBM DRAM Testing Methodology
6. Conclusion
Notes: I will talk about HBM DRAM Organization next.

## Slide 300: System with High Bandwidth Memory
Compute Chip (e.g., FPGA)
Memory Chip (e.g., HBM DRAM)
Inside one package
https://www.hpcwire.com/off-the-wire/xilinx-adds-high-bandwidth-memory-capabilities-to-its-virtex-ultrascale-portfolio/
Notes: A typical HBM2 DRAM system [CLICK] consists of a compute chip and multiple HBM2 DRAM chips.
[CLICK] All of these chips are integrated into a single package to form the HBM2 system.

## Slide 301: HBM DRAM Organization (I)
Memory Controller
FPGA
Silicon Interposer
HBM DRAM Chip
HBM Interface
Buffer Die (Logic Die)
Through-Silicon Vias (TSVs)
Channel
Channel
TSVs
DRAM Dies
Channel
Channel
TSVs
Channel
Channel
TSVs
Notes: Here is a different view of the same HBM system
[CLICK] The FPGA and the HBM chips reside in the same package and are connected by a Silicon Interposer
[CLICK] The memory controller in the FPGA communicates with the buffer die in the 3D-stacked HBM chip
[Click] over the HBM interface
[CLICK] The HBM2 chip contains multiple 3D-stacked DRAM dies
[CLICK] Each DAM die contains one or multiple DRAM channels
[CLICK] High-speed through silicon vias connect the 3D-stacked channels to the buffer die

## Slide 302: HBM DRAM Organization (I)
Memory Controller
FPGA
Silicon Interposer
HBM2 DRAM Chip
HBM2 Interface
Buffer Die (Logic Die)
Through-Silicon Vias (TSVs)
Channel
Channel
TSVs
DRAM Dies
Channel
Channel
TSVs
Channel
Channel
TSVs
Notes: Let’s now look at what is inside a DRAM channel

## Slide 303: HBM DRAM Organization (II)
DRAM Channel
Pseudo-Channel
TSVs
DRAM Bank
Subarray
. . .
DRAM Subarray
Row of DRAM cells
Row 1
Row 2
Row 3
Row 4
Bank
Notes: An HBM DRAM channel contains multiple pseudo-channels and each pseudo-channel contains multiple banks [CLICK]
Each bank is composed of multiple subarrays [CLICK]
And a subarray consists of many DRAM rows. [CLICK]
Each DRAM row contains many DRAM storage cells.

## Slide 304: Outline
1. HBM DRAM Organization & Operation
2. DRAM Cell Leakage & RowHammer
4. RowHammer Spatial Variation Analysis
5. On-die RowHammer Mitigation Analysis
3. HBM DRAM Testing Methodology
6. Conclusion
Notes: Let’s look at leakage in DRAM cells and the RowHammer phenomenon in more detail.
=========
Flow better: “Now let’s lok at a cell, its leakgea and rowhammer in more detail”

## Slide 305: DRAM Cell Leakage
Each cell encodes information in leaky capacitors
wordline
capacitor
access
transistor
bitline
Stored data is corrupted if too much charge leaks (i.e., the capacitor voltage degrades too much)
charge
leakage
paths
[Patel+, ISCA’17]
Notes: Each cell encodes data in fundamentally leaky capacitors [CLICK] Here is a simplified diagram of a DRAM cell, where the capacitor in red stores the data and the access transistor gates access to the data
[CLICK]
There are a number of leakage paths by which charge can enter or exit the capacitor.
[CLICK]
The important thing to note is that stored data can be corrupted if too much charge leaks
Which is the same as saying if the capacitor voltage degrades too much
[END]

## Slide 306: DRAM Refresh
Periodic refresh operations preserve stored data
Capacitor voltage (Vdd)
100%
0%
Vmin
Refresh Window
Refresh Operations
time
REF
REF
REF
Notes: Here, we have a simplified diagram of the capacitor voltage over time
We see that the voltage decreases over time in an exponential decay.
There’s a threshold Vmin under which we can no longer guarantee that we will correctly read the data that was originally stored in the cell.
[CLICK]
As long as a cell’s voltage remains above this line, we consider this a retention success.
[CLICK]
However, as soon as the voltage drops below Vmin, we consider this a retention failure
In order to prevent charge leakage failures, also known as retention failures, [CLICK] we issue periodic refresh operations to restore the charge in the cell. [CLICK] The interval between refresh commands are referred to as the refresh window.

## Slide 307: RowHammer Bitflips
Capacitor voltage (Vdd)
100%
0%
Vmin
time
REF
REF
REF
RowHammer Attack:
Accesses to nearby row
RowHammer
Bitflip
Notes: Now lets take a look at this diagram in the context of a RowHammer attack.
[CLICK] If enough activations are issued to a nearby row within a refresh window, the charge leakage rate can be accelerated to the point of failure.
Subsequent refresh commands now see this bit as a 0 value and maintain the discharged state of the cell

## Slide 308: Problem & Goal
No prior study demonstrates the RowHammer vulnerability in high bandwidth memory
Experimentally analyze how vulnerable real high bandwidth memory chips are to RowHammer
Our Goal
Problem
Notes: Let me re-iterate the problem we are tackling in our work.
No prior work rigorously studies the RowHammer vulnerability in high bandwidth memory
[CLICK] and our goal is to experimentally analyze how vulnerable real hbm chips are to RowHammer

## Slide 309: Outline
1. HBM DRAM Organization & Operation
2. DRAM Cell Leakage & RowHammer
4. RowHammer Spatial Variation Analysis
5. On-die RowHammer Mitigation Analysis
3. HBM DRAM Testing Methodology
6. Conclusion
Notes: I will now introduce the testing methodology we use in our experimental analysis

## Slide 310: DRAM Testing Infrastructure
DRAM Bender DDR3/4 Testing Infrastructure
Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips," in TCAD, 2023.
Adapt to work with HBM2 chips
https://github.com/CMU-SAFARI/DRAM-Bender
Notes: Our infrastructure is based on DRAM Bender DDR3/4 testing infrastructure.
[CLICK] We adapt DRAM Bender to work with HBM2 chips

## Slide 311: DRAM Testing Infrastructure
FPGA-based HBM2 Testing Setup (Bittware XUPVVH)
Fine-grained control over DRAM commands,
timing parameters (±1.66ns)
Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips," in TCAD, 2023.
Notes: Here is a photo of our testing setup.
We use the Bittware XUPVVH HBM2 FPGA board.
We control the heating pad and the cooling fan using the Arduino temperature controller to keep the temperature of the testing setup stable.
[CLICK] This setup gives us fine-grained control over DRAM commands and we can have as low as a 1.66 ns delay between two consecutive DRAM commands we issue to the HBM chip.

## Slide 312: RowHammer Testing Methodology (I)
To characterize our DRAM chips at worst-case conditions:
Prevent sources of interference during core test loop
  No DRAM refresh: to avoid refreshing victim row
  No RowHammer mitigation mechanisms: to observe circuit-level effects
  Test for less than a refresh window (32ms) to avoid retention failures
  Repeat tests for five times
Worst-case RowHammer access sequence
We use worst-case RowHammer access sequence based on prior works’ observations
Double-sided RowHammer: repeatedly access the two physically-adjacent rows as fast as possible
Record bitflips in victim
Victim Row
Aggressor Row 1
Aggressor Row 2
Notes: [CLICK x8]
We carefully re-use the rigorous RowHammer characterization methodology described in prior work where we prevent sources of interference and use the worst-case double-sided RowHammer access patterns.
==========
Go over quickly: We use the methodology in prior work and zap thru animations
Record bitflips everywhere for future works  add to google docs
To characterize our DRAM chips at worst-case conditions we take two measures:
[CLICK] First, we prevent external sources of interference such that our tests can run consistently as desired and without interruptions. To achieve this we disable:
[CLICK] DRAM refresh to avoid refreshing victim rows during a test,
[CLICK] and RowHammer mitigation mechanisms to ensure that we can directly observe circuit-level bit flips
[CLICK] we also ensure that our RowHammer tests complete in less than a refresh window to prevent retention failures from interfering with our results
[CLICK] and we repeat our tests five times to filter out the noise in measurements
[CLICK] Second, we issue the worst-case access sequence for inducing RowHammer bit flips based on observations from prior work
[CLICK] where we repeatedly activate the two physically-adjacent rows as fast as possible to perform double-sided RowHammer on a victim row
[CLICK] Finally, we record the bitflips induced on the victim row.

## Slide 313: RowHammer Testing Methodology (II)
Tested HBM2 chip’s organization:
  8 channels
  2 pseudo-channels
  16 banks
  16384 rows (1 KiB each)
Test all channels, pseudo-channels, banks
Test first, middle, and last 3K rows in a bank
  9K out of 16K (more than half)
Keep HBM2 chip temperature at 85°C
Xilinx FPGA with HBM2 DRAM chips
Notes: [CLICK] Our HBM2 chip contains 8 channels, 2 pseudo-channels in each channel, 16 banks in each pseudo-channel, and around 16 thousand 1 KiB large rows.
[CLICK] We test all channels, pseudo-channels, and banks
[CLICK] We sample the first, middle, and last 3K rows in a bank for our experiments.
[CLICK] and we set the temperature controller’s target temperature to 85 degree celcius

## Slide 314: Metrics
Bit error rate (BER): The fraction of DRAM cells in a row that experience a bitflip after 512K activations
Hammer Count for the First Bitflip (HCfirst): Aggressor row activation count to cause the first bitflip in the victim row
Higher is worse
Lower is worse
Notes: We measure two metrics:
[CLICK] The bit error rate is the fraction of cells in a DRAM row that experience a bitflip. We activate the aggressor rows 512 thousand times for this. We say that RowHammer vulnerability worsens as this metric becomes higher.
[CLICK] The hammer count for the first bitflip is the number of aggressor row activations required to cause the first bitflip in the victim row. As this metric becomes smaller, it means that we need a shorter time to induce a RowHammer bitflip.

## Slide 315: Tested Data Patterns
00000000000000000000000
11111111111111111111111
11111111111111111111111
00000000000000000000000
00000000000000000000000
00000000000000000000000
00000000000000000000000
…
…
…
…
…
…
Notes: We use the data patterns depicted in this table to initialize DRAM rows prior to performing RowHammer.
I will explain how data gets laid out to DRAM rows based on the first Rowstripe0 data pattern:
[CLICK] We fill the victim row with all zeros,
[CLICK] The aggressors with all ones
[CLICK] And the 7 other rows neighboring each aggressor with all zeros

## Slide 316: Tested Data Patterns
10101010101010101010101
01010101010101010101010
01010101010101010101010
10101010101010101010101
10101010101010101010101
10101010101010101010101
10101010101010101010101
…
…
…
…
…
…
Notes: Here is another example showing what happens when we use the checkered0 data pattern

## Slide 317: Tested Data Patterns
10101010101010101010101
01010101010101010101010
01010101010101010101010
10101010101010101010101
10101010101010101010101
10101010101010101010101
10101010101010101010101
…
…
…
…
…
…
Worst-case data pattern (WCDP) of a row: Causes smallest HCfirst for a row
Notes: We use these four different data patterns
[CLICK] and we determine the worst-case data pattern for each tested DRAM row as the data pattern that causes the smallest Hcfirst value for that row
[CLICK] note that this worst-case data pattern is always one of the four tested data patterns

## Slide 318: Two Main Analyses
1. Spatial variation of RowHammer vulnerability
How does the RowHammer vulnerability change across channels, pseudo-channels, banks, rows in HBM?
2. On-DRAM-die RowHammer mitigations
Do real HBM chips implement undisclosed RowHammer mitigations resembling those that exist in DDR4?
DRAM Channel
Pseudo-Channel
TSVs
DRAM Bank
Subarray
. . .
DRAM Subarray
Row of DRAM cells
Row 1
Row 2
Row 3
Row 4
Bank
Notes: We provide two main analyses in our study
[CLICK] We investigate how RowHammer vulnerability changes across different HBM components in terms of bit error rate and activation count to induce the bitflip.
[CLICK] and we investigate if the HBM chip implements undisclosed RowHammer mitigations that resemble the ones in real DDR4 chips.

## Slide 319: Outline
1. HBM DRAM Organization & Operation
2. DRAM Cell Leakage & RowHammer
4. RowHammer Spatial Variation Analysis
5. On-die RowHammer Mitigation Analysis
3. HBM DRAM Testing Methodology
6. Conclusion
Notes: I will first share the results of our RowHammer Spatial Variation analysis

## Slide 320: Key Takeaways from Spatial Variation Analysis
Different 3D-stacked HBM2 channels exhibit different RowHammer vulnerability
Takeaway 1
DRAM rows near the end of a DRAM bank experience smaller bit error rate (BER) than others
Takeaway 2
Activation count needed to induce the first RowHammer bitflip (HCfirst) changes with the data pattern and the physical location of the DRAM row
Takeaway 3
Notes: Starting with the three key takeaways we make from our analysis
First, Different 3D-stacked channels exhibit different RowHammer vulnerability
[CLICK] Second, DRAM rows near the end of a DRAM bank experience smaller bit error rate than other rows
[CLICK] Third, the activation count needed to induce the first RowHammer bitflip changes with the data pattern and the physical location of the DRAM row

## Slide 321: Spatial Distribution of BER (I)
There are bitflips in every tested DRAM row across all tested HBM2 channels
BER varies across channels: groups of two channels have different BERs
Notes: This figure depicts the RowHammer bit error rate distribution across all tested rows on the y-axis and the data patterns we use on the x-axis.
Different bars show the distribution of bit error rate in different HBM2 DRAM channels
We make two observations from this figure.
[CLICK] First, we observe bitflips in every tested DRAM row in all tested channels.
[CLICK] Second, BER varies across channels. We find that groups of two channels have different bit error rates compared to other groups.

## Slide 322: Spatial Distribution of BER (I)
The data pattern affects the BER distribution
Up to ~262 bitflips in a row of 8K bits with 512K aggressor row activations
~262 bitflips (out of 8192 in a row)
Notes: [CLICK] We see that the data pattern has an affect on the distribution of the bit error rate and that our observations are consistent across different data patterns.
[CLICK] I highlight the distributions we get for the worst-case data pattern. We observe up to around 262 bitflips in a row of 8K bits with 512K hammers.

## Slide 323: Spatial Distribution of BER (II)
BER periodically increases and decreases across rows: BER is higher in the middle of a subarray
BER is substantially smaller in the last subarray (i.e., last 832 rows)
SA start
SA end
Last subarray (SA)
Notes: This plot shows the bit error rate on the y–axis and row addresses on the x-axis. Different lines show the bit error rate for different channels
Note that we show the last 3 thousand rows on the x-axis.
The dashed vertical lines indicate reverse-engineered subarray boundaries. Because we show only the last 3K rows, the first subarray on the left is not shown completely in this figure.
[CLICK] We observe that the bit error rate is substantially smaller in the last subarray compared to other subarrays.
[CLICK] We also see that the bit error rate goes up and down as row addresses increase. The bit error rate is the higheset in the middle of a subarray and lowest at either ends of a subarray. We will explain this later in more detail.
===================
How do you reverse engineer subarray boundaries?

## Slide 324: Spatial Distribution of BER (II)
BER periodically increases and decreases across rows: BER is higher in the middle of a subarray
BER is substantially smaller in the last subarray (i.e., last 832 rows)
Notes: We show the same plot for the first and the middle 3K rows.
We see that our second observation is valid for all tested DRAM rows.

## Slide 325: Spatial Distribution of HCfirst
HCfirst is as low as 14531 across all tested rows/channels: Only ~1.3 ms to induce a RowHammer bitflip
HCfirst distribution heavily depends on the data pattern
Notes: This plot shows the Hcfirst distribution across rows in each channel on the y-axis and the data patterns on the x-axis. We use different boxes to plot hcfirst distributions for different channels.
[CLICK] We observe that Hcfirst is as low as around 14 thousand across all rows. This means that we can induce a bitflip in only around 1 milisecond.
[CLICK] We see that the Hcfirst distribution depends heavily on the data pattern we use to initialize DRAM rows.

## Slide 326: Variation in Bit Error Rate
Banks in the same channel have similar variation in BER
Small distance on x and y axes
Large distance on x and y axes
Two different banks in the same channel
Notes: We also investigate the variation in BER across rows in each bank but I have to skip this due to time limits. I am happy to answer any questions on this.

## Slide 327: Hypotheses from Characterization
Similar BER & HCfirst within groups of two channels suggests these channels share DRAM dies
RowHammer BER changes with the row’s proximity to sense amplifiers and bank I/O
Notes: We form two key hypotheses from our characterization study
[CLICK] First, we attribute the similarity in bit error rate and hcfirst within groups of two channels to their physical placement inside the HBM chip. We think that groups of two channels share the same DRAM die.
[CLICK] Second, RowHammer bit error rate changes with the row’s proximity to sense amplifiers. We think that the significant drop in bit error rate in the last subarrays can be due to the subarray’s proximity to bank I/O logic.

## Slide 328: Implications on Attacks and Mitigations
Two implications for RowHammer attacks and mitigations
Key Observation: RowHammer BER and HCfirst vary across channels
A RowHammer attack can use the most-RH-vulnerable HBM2 channel to prepare for and perform the attack faster
A RowHammer mitigation can allocate fewer resources for RowHammer-resilient channels and
more efficiently prevent RowHammer bitflips
Notes: We make this key observation from our study.
[CLICK] This has two implications for RowHammer attacks and mitigations
[CLICK] First, attacks can use the most vulnerable channels to accelerate their preparation and attack phases. This allows an attacker to take over vulnerable systems more quickly.
[CLICK] Second, mitigations can allocate fewer resources to protect RowHammer-resilient channels and more resources to protect RowHammer-vulnerable channels. This would allow for more efficient RowHammer mitigation mechanisms.

## Slide 329: Outline
1. HBM DRAM Organization & Operation
2. DRAM Cell Leakage & RowHammer
4. RowHammer Spatial Variation Analysis
5. On-die RowHammer Mitigation Analysis
3. HBM DRAM Testing Methodology
6. Conclusion
Notes: I will now describe our second main analysis on on-DRAM-die RowHammer mitigations

## Slide 330: Key Takeaways from on-die Mitigation Analysis
A modern HBM2 chip implements an undisclosed on-DRAM-die RowHammer mitigation
Takeaway 1
This mitigation resembles the one in DDR4 chips from one major manufacturer as shown in prior work
Takeaway 2
Hassan et al., "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications,” in MICRO, 2021.
Notes: Here are the two key takeaways from our study
First, the chip we test implements an undisclosed on-DRAM-die RowHammer mitigation mechanism
[CLICK] Second, this mitigation resembles the ones prior work has found in real DDR4 chips
===========================
Add reference to uTRR
How does U-TRR know beyond “every 17 refresh”?

## Slide 331: On-Die RowHammer Mitigation Analysis (I)
HBM2 standard defines a “Target Row Refresh (TRR)-mode”
Memory controller and DRAM cooperate to prevent RH bitflips
Real DDR4 chips implement on-die mitigation mechanisms
Memory-controller-transparent, hidden behind periodic REF
Does a similar hidden mitigation mechanism exist in HBM2?
Notes: The HBM2 standard defines a Target Row Refresh mode where the controller and the HBM chip cooperates to prevent RowHammer bitflips
[CLICK] However, we also know that real DDR4 chips implement on-die mitigation mechanisms that take actions in a memory-controller-transparent way, typically hidden behind the latency of a periodic refresh operation
[CLICK] We want to understand if a similar hidden mitigation mechanism exists in our HBM2 chip.

## Slide 332: On-Die RowHammer Mitigation Analysis (II)
Key idea: Use data retention failures as a side channel
to detect when a row is refreshed by on-die mitigation
[Hassan+, MICRO’21, source code available at https://github.com/CMU-SAFARI/U-TRR]
Hassan et al., "Uncovering In-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications,” in MICRO, 2021.
Notes: We use the methodology presented in this paper
[CLICK] Where the key idea is to use data retention failures as a side channel to detect when a row is refreshed by the on-die mitigation mechanism
[CLICK] We re-use the source code that is publicly available on this Github page.

## Slide 333: Experimental Methodology
[Hassan+, MICRO’21]
Victim Row R
1. Identify a row (R) with T retention time
2. Wait for T/2
Aggressor Row R + 1
3. Hammer R+1 once
4. Issue a periodic REF command (trigger mitigation)
5. Wait for T/2, read out row R and check for bitflips
On-DRAM-die Mitigation
Sample as aggressor row
Timeline
Refresh R
time = 0
time = T/2
time = T
Read R
Refresh victim row
Mitigation refreshes R
Notes: Our experiment first
[CLICK] finds a DRAM row R with a retention time of T. This means that the row will harbor retention failures if we do not refresh its content for T units of time.
[CLICK] On the bottom we show a timeline of actions taken by us and the currently-hypothetical on-die mitigation mechanism. Initially, the row R is refreshed, so it can retain data correctly until time is T.
[CLICK] We wait for half T.
[CLICK] We activate and precharge R+1 (which is adjacent to R) once.
[CLICK] Let’s now look at what a hypothetical on-die mitigation would do
[CLICK] It will sample the hammering of R+1 as an aggressor row activation
[CLICK] after which we issue a periodic refresh command (to trigger the mitigation)
[CLICK] If the mitigation sampled R+1 as an aggressor row, it will refresh R as the victim row
[CLICK] We then wait for half T, read out row R and check for bitflips in row R.

## Slide 334: Experimental Methodology
[Hassan+, MICRO’21]
Victim Row R
1. Identify a row (R) with T retention time
2. Wait for T/2
Aggressor Row R + 1
3. Hammer R+1 once
4. Issue a periodic REF command (trigger mitigation)
5. Wait for T/2, read out row R and check for bitflips
On-DRAM-die Mitigation
Sample as aggressor row
Refresh victim row
Timeline
Refresh R
time = 0
time = T/2
time = T
Row R experiences no bitflips only if on-DRAM-die mitigation exists
Mitigation refreshes R
Read R
Notes: Row R will not experience any bitflips
Only if on-DRAM-die mitigation exists and has refreshed R at half T

## Slide 335: Experimental Methodology
[Hassan+, MICRO’21]
Victim Row R
1. Identify a row (R) with T retention time
2. Wait for T/2
Aggressor Row R + 1
3. Hammer R+1 once
4. Issue a periodic REF command (trigger mitigation)
5. Wait for T/2, read out row R and check for bitflips
On-DRAM-die Mitigation
Sample as aggressor row
Refresh victim row
Timeline
Refresh R
time = 0
time = T
Row R experiences no bitflips only if on-DRAM-die mitigation exists
Read R
Row R experiences retention bitflips if not refreshed at T/2
retention bitflips
time = T/2
Row R not refreshed
Notes: Otherwise, row R will experience retention bitflips because it was not refreshred for T units of time.

## Slide 336: HBM2 DRAM Chips Implement Undisclosed TRR
The HBM2 chip implements an undisclosed on-die RowHammer mitigation mechanism
This mechanism performs a victim row refresh operation every 17 periodic refresh (REF) operations
This mitigation resembles the one in DDR4 chips from one major manufacturer
Notes: We perform this experiment and find that
[CLICK] the HBM2 chip implements an undisclosed on-die mitigation mechanism
[CLICK] This mechanism performs a victim row refresh operation after every 17 periodic refresh operations.
[CLICK] Which resembles a TRR mechanism implemented in real DDR4 chips from one major manufacturer.
We intend to uncover more about the inner workings of this TRR mechanism as part of our future work

## Slide 337: Outline
1. HBM DRAM Organization & Operation
2. DRAM Cell Leakage & RowHammer
4. RowHammer Spatial Variation Analysis
5. On-die RowHammer Mitigation Analysis
3. HBM DRAM Testing Methodology
6. Conclusion
Notes: I will conclude my talk with a brief summary

## Slide 338: Conclusion
We provide the first detailed experimental characterization of RowHammer in a modern HBM2 DRAM chip
Different channels in 3D-stacked HBM chips exhibit different RowHammer vulnerability
DRAM rows near the end of a DRAM bank are more RowHammer resilient
Two implications for RowHammer attacks and mitigations:
Faster and more effective attacks
More efficient mitigations
A modern HBM chip implements undisclosed on-DRAM-die RowHammer mitigation (e.g., similar to DDR4 chips)
Future Directions: To present more insights into how RowHammer behaves in HBM
Test more HBM DRAM chips, data patterns, at different temperature and voltage levels
Investigate read-disturb-based interference across different 3D-stacked HBM DRAM channels
Study the effects of the new read-disturb phenomenon, RowPress [Luo+, ISCA’23]
Luo et al., ”RowPress: Amplifying Read Disturbance in Modern DRAM Chips," in ISCA, 2023.
Notes: We provide the first detailed experimental characterization of RowHammer in a modern HBM2 DRAM chip
We find that
[CLICK] different channels exhibit different vulnerability, and
[CLICK] DRAM rows near the end of a bank are more resilient.
[CLICK] These findings can be leveraged to develop powerful attacks and more efficient defenses
[CLICK] We identify an on-die RowHammer mitigation mechanism in HBM2 chips. This mechanism resembles existing ones found in DDR4 chips.
[CLICK] To present more insights into RowHammer’s behavior in high bandwidth memory,
We plan to test more chips and data patterns, and at different temperature and voltage levels
[CLICK] Investigate the effects of read-disturb interference across 3D-stacked channels.
[CLICK] Study effects of new read-disturb phenomenon such as RowPress that was very recently presented at ISCA

## Slide 339: Available on ArXiv
https://arxiv.org/abs/2305.17918
Notes: A version of our conference paper is available on arXiv on this link.

## Slide 340
Ataberk Olgun Majd Osseiran
A. Giray Yağlıkçı
Yahya Can Tuğrul
Steve Rhyner
Haocong Luo
Juan Gomez Luna
Onur Mutlu
Behzad Salami
Link/QR code to full paper
https://arxiv.org/pdf/2305.17918
An Experimental Analysis of RowHammer in HBM2 DRAM Chips
Notes: Thank you very much for your attention. I will be happy to take your questions now.

## Slide 341: Extended version submitted to HPCA
Tests 5 more HBM2 chips
Tests more DRAM components (e.g., banks and rows) per chip
Analyzes hammer counts to induce more than one bitflip (HCsecond, third,… , tenth)
Analyzes the RowPress vulnerability of HBM2 chips
Further reverse engineers the on-DRAM-die RH defense mechanism

## Slide 342: Methodology

## Slide 343: RowHammer BER Across Chips

## Slide 344: RowHammer HCfirst Across Chips

## Slide 345: RowHammer BER Across Channels

## Slide 346: RowHammer HCfirst Across Channels

## Slide 347: RowHammer BER Across Rows

## Slide 348: RowHammer’s Sensitivity to Hammer Count (I)

## Slide 349: RowHammer’s Sensitivity to Hammer Count (II)

## Slide 350: RowPress BER Across Channels

## Slide 351: RowPress HCfirst Across Channels

## Slide 352: Attack Patterns to Bypass Undisclosed TRR

## Slide 353: Silicon Level RowHammer and RowPress Mechanisms

## Slide 354: Major RowHammer Silicon Mechanisms (I)
There are two major silicon-level causes for RowHammer bitflips [1, 7].
First, capacitive coupling between the physically-adjacent aggressor and victim wordlines causes crosstalk.
  When the aggressor wordline is activated, the potential of the victim wordlines also increases [10], causing an increase in the access transistor subthreshold leakage of the victim cell [1, 4].
  When the aggressor wordline is repeatedly activated many times, the accumulation of the increased subthreshold leakage causes bitflips.
Second, repeated switching of the channel of the access transistor of the aggressor cell injects electrons into the storage node of the victim cell, causing it to lose charge [1 - 5].
  The injected electrons mainly come from two sources.
  First, when the aggressor access transistor is switched off, the diffused channel electrons are attracted to the storage node of the victim cell [2, 3, 6, 8]. This is because the victim cell’s storage node has a higher potential compared to the bitline [2]. These electrons recombine with the stored charge in the victim cell, reducing the cell potential, and eventually causing a bitflip.
  Second, the interface charge traps of the aggressor access transistor traps electrons during the activation of the victim row [4, 5, 8]. Later, when the aggressor row is closed, the trapped electrons are released and find their way to the storage node of the victim cell.

## Slide 355: Major RowHammer Silicon Mechanisms (II)
Although existing literature [1-6] suggests that both capacitive crosstalk between wordlines and electron migration and injection are the two fundamental silicon-level mechanisms for RowHammer bitflips, they do not quantitatively compare the contribution of these two mechanisms to make out a dominant cause for RowHammer.
A recent work [9] investigates how each mechanism contributes to the significantly increased RowHammer vulnerability (i.e., requiring much less aggressor row activation to induce a bitflip) of the double-sided access pattern.
The key takeaway of [9] is that the trap-assisted electron migration & injection is the dominant mechanism for the increased vulnerability to double-sided RowHammer (i.e., requiring fewer aggressor row activations to induce a bitflip) compared to single-sided, while capacitive crosstalk is not a major factor in the increased vulnerability to double-sided RowHammer compared to single-sided.

## Slide 356: Silicon-Level RH: Pictorial Illustration (I)
Figure 1 illustrates the physical layout of DRAM.
Figure 2 shows how electrons are injected into the victim cell.
Figure 1. DRAM Physical Layout (Figurative)

## Slide 357: Silicon-Level RH: Pictorial Illustration (II)
Figure 2a) shows the initial state, where WL1 is the aggressor wordline and SN2 is the storage node of the victim cell, which is initially positively charged.
When the aggressor wordline is open (Figure 2b), excessive electrons are concentrated in the aggressor’s channel ① due to channel inversion and/or interface traps.
When the aggressor wordline is closed, the channel inversion layer collapses (and/or the trapped electrons get released), and some of the excessive electrons can migrate and inject into the victim cell ②.
Figure 2. Electron Migration & Injection (Figurative)

## Slide 358: RH Silicon Mechanism References
[1] Walker et al., “On DRAM Rowhammer and the Physics of Insecurity,” in IEEE Transactions on Electron Devices, 2021
[2] Park et al., “Experiments and root cause analysis for active-precharge hammering fault in DDR3 SDRAM under 3×nm technology,” in Microelectronics Reliability, 2016
[3] Yang et al., “Suppression of Row Hammer Effect by Doping Profile Modification in Saddle-Fin Array Devices for Sub-30-nm DRAM Technology,” in IEEE Transactions on Device and Materials Reliability, 2016
[4] Ryu et al., “Overcoming the Reliability Limitation in the Ultimately scaled DRAM using Silicon Migration Technique by Hydrogen Annealing,” in Technical Digest - International Electron Devices Meeting, IEDM, 2018
[5] Yang et al., “Trap-Assisted DRAM Row Hammer effect,” in IEEE Electron Device Letters, 2019
[6] Gautam et al., “Row Hammering Mitigation Using Metal Nanowire in Saddle Fin DRAM,” in IEEE Transactions on Electron Devices, 2019
[7] Han et al., “Surround Gate Transistor With Epitaxially Grown Si Pillar and Simulation Study on Soft Error and Rowhammer Tolerance for DRAM,” in IEEE Transactions on Electron Devices, 2021
[8] Park et al., “Row Hammer Reduction Using a Buried Insulator in a Buried Channel Array Transistor,” in IEEE Transactions on Electron Devices, 2021
[9] Zhou et al., “Double-sided Row Hammer Effect in Sub-20 nm DRAM: Physical Mechanism, Key Features and Mitigation,” in IEEE International Reliability Physics Symposium (IRPS), 2023
[10] Redeker et al., “An Investigation into Crosstalk Noise in DRAM Structures,” in Proceedings of the 2002 IEEE International Workshop on Memory Technology, Design and Testing (MTDT), 2002

## Slide 359: Major RowPress Silicon Mechanism
RowPress causes bitflips by keeping the aggressor row open for a long period of time. One silicon-level mechanism to explain RowPress is called the passing gate effect [11, 12].
Figure 3 shows how the passing gate effect causes bitflips.
In the initial state (Figure 3.a), SN2 is the victim and the passing wordline PWL2 is the aggressor. The victim cell is initially negatively charged.
When PWL2 is kept open (Figure 3.b), it keeps attracting electrons from the victim cell ①.
When PWL2 is closed (Figure 3.c), not all the attracted electrons will return to the victim cell, causing leakage.

## Slide 360: RP Silicon Mechanism References
[11] Hong et al., “DSAC: Low-Cost Rowhammer Mitigation Using In-DRAM Stochastic and Approximate Counting Algorithm,” arXiv:2302.03591 [cs.CR]
[12] Nam et al., “X-ray: Discovering DRAM Internal Structure and Error Characteristics by Issuing Memory Commands,” in IEEE CAL, 2023

## Slide 361: Illustrations

## Slide 362: Silicon-Level Disturbance Mechanism
Electron Migration & Injection
Figurative illustration of the physical layout of a DRAM cell
Wordline
Bitline
Active Region
Storage Node (SN)
Bitline
Contact
Cell
Capacitor
WL
Channel
Top View
Cross Section
P-Well
n+
BL
SN

## Slide 363: Silicon-Level Disturbance Mechanism
Electron Migration & Injection
High-level: Electrons migrate from the aggr channel to the victim node
Wordline
Bitline
Active Region
Storage Node (SN)
Bitline
Contact
Cell
Aggr
WL
Top View
Cross Section
BL
e-
e-
Electron Migration
Injection
Aggr WL
Victim

## Slide 364: Silicon-Level Disturbance Mechanism
Electron Migration & Injection
High-level: Electrons migrate from the aggr channel to the victim node
Sources of these electrons
  Collapse of the inversion layer of the aggressor row’s access transistor channel when the aggressor WL is turned off
  Interface traps at the aggressor WL that capture electrons when the aggressor WL is open, and release them when the aggressor WL is off

## Slide 365: Silicon-Level Disturbance Mechanism
Electron Migration & Injection
Inversion layer collapse in the aggr channel
Aggr
WL
Aggressor WL On
BL
Victim
e-
e-
e-
e-
e-
e-
e-
Aggr
WL
Aggressor WL Off
BL
Victim
e-
e-
e-
e-
e-
e-
e-
Precharge

## Slide 366: Silicon-Level Disturbance Mechanism
Electron Migration & Injection
Interface charge trap
Aggr
WL
BL
Victim
Aggr
WL
Trap charged
BL
Victim
Interface Charge Trap
ACT
e-
e-
e-
Initial state

## Slide 367: Silicon-Level Disturbance Mechanism
Electron Migration & Injection
Interface charge trap
Aggr
WL
Charge released
BL
Victim
PRE
Aggr
WL
Trap charged
BL
Victim
e-
e-
e-
e-
e-
e-

## Slide 368: Silicon-Level Disturbance Mechanism
Passing Gate Effect
Figurative illustration of the physical layout of a DRAM cell
Wordline
Bitline
Active Region
Storage Node (SN)
Bitline
Contact
Capacitor
WL
Channel
Top View
Cross Section
BL
SN
Passing WL
Passing WL
Isolation Field Oxide

## Slide 369: Silicon-Level Disturbance Mechanism
Passing Gate Effect
Attracts electrons from the victim
Initial state
Passing WL
Victim
e-
e-
e-
e-
Passing WL On
Passing WL
Victim
e-
e-
e-
e-

## Slide 370: Silicon-Level Disturbance Mechanism
Passing Gate Effect
Attracts electrons from the victim
Passing WL Off
(Some electrons do not return to the victim)
Passing WL
Victim
e-
e-
e-
e-
Passing WL On
Passing WL
Victim
e-
e-
e-
e-

## Slide 371: Silicon-Level Disturbance Mechanism
Passing Gate Effect
The longer the passing WL is open, the more electrons it can attract from the victim.
Major contributor to the RowPress vulnerability.

## Slide 372: Access Pattern - RowHammer
Single-Sided - Case 1
A
V
Contributing mechanisms
Increased subthreshold leakage due to AWL-VWL crosstalk
Electron migration and injection from aggressor channel to victim node
“Normal” leakage as time passes by

## Slide 373: Access Pattern - RowHammer
Single-Sided - Case 2
A
V
Contributing mechanisms
Increased subthreshold leakage due to AWL-VWL crosstalk (?)
Passing gate effect
“Normal” leakage as time passes by

## Slide 374: Access Pattern - RowHammer
Double-Sided
A2
V
Contributing mechanisms
Increased subthreshold leakage due to AWL-VWL crosstalk
Electron migration & injection from A1
Passing gate effect from A2
“Normal” leakage as time passes by
A1

## Slide 375: Access Pattern - RowHammer
Half-Double
Many Far Aggressor (FA) activations followed by only a few Near Aggressor (NA) activations causes bitflips in the Victim (V)
FA
NA
Hypothesized mechanisms
Frequent FA activation accumulates electrons near the NA side
Few NA activations causes those electrons to migrate and inject into V
V
e-
e-
e-
e+
e+
e+

## Slide 376: Access Pattern - RowHammer
Half-Double
Many Far Aggressor (FA) activations followed by only a few Near Aggressor (NA) activations causes bitflips in the Victim (V)
FA
NA
Hypothesized mechanisms
Frequent FA activation accumulates electrons near the NA side
Few NA activations causes those electrons to migrate and inject into V
V
e-
e-
e+
e+
e+
e-

## Slide 377: Access Pattern - RowHammer
Half-Double
Many Far Aggressor (FA) activations followed by only a few Near Aggressor (NA) activations causes bitflips in the Victim (V)
FA
NA
Hypothesized mechanisms
Frequent FA activation accumulates electrons near the NA side
Few NA activations causes those electrons to migrate and inject into V
V
e-
e-
e+
e+
e+
e-

## Slide 378: Access Pattern - RowHammer
Half-Double
Another case…?
FA
NA
V
No hypothesized mechanisms so far…

## Slide 379: Ongoing Works

## Slide 380: ABACuS: All-Bank Activation Counters for Scalable and Low Overhead RowHammer Mitigation USENIX Security 2024
Ataberk Olgun
21.09.2023

## Slide 381: Executive Summary
Problem: RowHammer vulnerability worsens as DRAM becomes denser
Existing defenses become more costly
Benign workloads frequently trigger performance-degrading RowHammer mitigations
Goal: Prevent RowHammer bitflips at low performance, energy, and area cost
Key Observation: Workloads tend to access the same row in all DRAM banks at around the same time
Key Idea: Use one hardware counter to keep track of activation counts of the same row across all banks
Make high-performance, area-hungry counter-based mechanisms practical
Key Results: Memory system simulations using 62 single core and 62 8-core workloads
At all tested RowHammer thresholds (1000, 500, 250 125):
Faster than the lowest-area-cost counter-based defense mechanism Smaller than the lowest-performance-overhead counter-based defense mechanism
0.59% avg. performance overhead (single-core) at a future RowHammer threshold (1K)
Only 9.79 KiB on-chip storage per DRAM rank (0.02% of a Xeon processor)
1.52% avg. performance overhead (single-core) at an ultra-low threshold (125)
75.70 KiB on-chip storage per DRAM rank (0.11% of the Xeon processor)

## Slide 382: RowHammer in HBM Chips (2023)
Ataberk Olgun, Majd Osserian, A. Giray Yağlıkçı, Yahya Can Tugrul, Haocong Luo, Steve Rhyner, Behzad Salami, Juan Gomez-Luna, and Onur Mutlu, "An Experimental Analysis of RowHammer in HBM2 DRAM Chips" Proceedings of the 53nd Annual IEEE/IFIP International Conference on Dependable Systems and Networks Disrupt Track (DSN Disrupt), Porto, Portugal, June 2023. [arXiv version] [Slides (pptx) (pdf)] [Talk Video (24 minutes, including Q&A)]
https://arxiv.org/pdf/2305.17918.pdf

## Slide 383: Executive Summary
Motivation: HBM chips have new architectural characteristics (e.g., 3D-stacked dies) that might affect the RowHammer vulnerability in various ways
Understanding RowHammer enables designing effective and efficient solutions
Problem: No prior study demonstrates the RowHammer vulnerability in HBM
Goal: Experimentally analyze how vulnerable HBM DRAM chips are to RowHammer
Experimental Study: Detailed experimental characterization of RowHammer in a modern HBM2 DRAM chip. Our study provides two main findings:
1. Spatial variation of RowHammer vulnerability
Different channels in a 3D-stacked HBM chip exhibit different RowHammer vulnerability
DRAM rows near the end of a DRAM bank are more RowHammer resilient
2. On-DRAM-die RowHammer mitigations
A modern HBM chip implements undisclosed on-DRAM-die RowHammer mitigation
The mitigation refreshes a victim row after every 17 periodic refresh operations (e.g., similar to DDR4 chips)
Notes: HBM chips harbor new architectural characteristics that might affect the RowHammer vulnerability
[CLICK] Understanding RowHammer enables designing effective and efficient solutions
[CLICK] However, no rigorous study demonstrates the RowHammer vulnerability in HBM
[CLICK] Our goal is to experimentally analyze how vulnerable real HBM chips are to RowHammer
[CLICK] Therefore, we perform a detailed experimental characterization of RowHammer in a modern HBM2 DRAM chip and we provide two main findings.
[CLICK] First, we show that there is substantial variation in RowHammer vulnerability in different physical locations of high bandwidth memory chips. Different channels in 3D-stacked HBM chips exhibit different vulnerability, and
[CLICK] DRAM rows near the end of a DRAM bank are more RowHammer resilient
[CLICK] Second, we show that a modern HBM chip implements undisclosed on-DRAM-die Rowhammer mitigation
[CLICK] We find that this particular mitigation refreshes a victim row after every 17 periodic refresh operations, resembling a mitigation prior work found in DDR4 chips

## Slide 384: Ongoing and Future Work
Discover New Bitflips
Fundamentally Fix Them
To Build More Robust Systems for Future

## Slide 385: Removed Slides

## Slide 386: How Reliable/Secure/Safe is This Bridge?
Source: http://www.technologystudent.com/struct1/tacom1.png

## Slide 387: Collapse of the “Galloping Gertie”
Source: AP
http://www.wsdot.wa.gov/tnbhistory/connections/connections3.htm

## Slide 388: How Safe & Secure Are These People?
Source: https://s-media-cache-ak0.pinimg.com/originals/48/09/54/4809543a9c7700246a0cf8acdae27abf.jpg
Security is about preventing unforeseen consequences

## Slide 389: How Safe & Secure Are Our Platforms?
Source: https://taxistartup.com/wp-content/uploads/2015/03/UK-Self-Driving-Cars.jpg
Security is about preventing unforeseen consequences

## Slide 390: Collapse of the “Galloping Gertie” (1940)
Source: AP
http://www.wsdot.wa.gov/tnbhistory/connections/connections3.htm

## Slide 391: Another Example (1994)
Source: By 최광모 - Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=35197984

## Slide 392: Yet Another Example (2007)
Source: Morry Gash/AP,
https://www.npr.org/2017/08/01/540669701/10-years-after-bridge-collapse-america-is-still-crumbling?t=1535427165809

## Slide 393: A More Recent Example (2018)
Source: AFP / Valery HACHE, https://www.capitalfm.co.ke/news/2018/08/genoa-bridge-collapse-what-we-know/

## Slide 394: A Most Recent Example (2022)
https://www.post-gazette.com/local/city/2022/01/28/pittsburgh-bridge-collapse-forbes-braddock-avenue-point-breeze-squirrel-hill/stories/202201280075

## Slide 395: A Most Recent Example (2022)
https://www.reuters.com/world/us/biden-highlight-manufacturing-jobs-gdp-growth-pittsburgh-2022-01-28/

## Slide 396: A Most Recent Example (2022)
https://usa.streetsblog.org/2022/01/28/pittsburgh-bridge-collapse-underscores-urgent-need-for-fix-it-first-policy/

## Slide 397: A Most Recent Example (2022)
https://www.npr.org/2022/01/28/1076343656/pittsburgh-bridge-collapse-biden-visit