## Slide 1: Accelerating Genome Analysis A Primer on an Ongoing Journey
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
3 November 2022
Montenegro Academy of Sciences Conference

## Slide 2: Overview
System design for bioinformatics is a critical problem
  It has large scientific, medical, societal, personal implications
This talk is about accelerating a key step in bioinformatics: genome sequence analysis
  In particular, read mapping
Many bottlenecks exist in accessing and manipulating huge amounts of genomic data during analysis
Many recent ideas to accelerate read mapping
  My personal journey since September 2006

## Slide 3: Our Dream (circa 2007)
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
  Which of these DNAs does this DNA segment match with?
  What is the likely genetic disposition of this patient to this drug?
  What disease/condition might this particular DNA/RNA piece associated with?
  . . .

## Slide 4: We Need Faster & Scalable Genome Analysis
Predicting the presence and relative abundance of microbes in a sample
Understanding genetic variations, species, evolution, …
Rapid surveillance of disease outbreaks
Developing personalized medicine
And, many, many other applications …
Notes: Knowing what organisms are present in a given environmental sample and how abundant are they

## Slide 5: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 6: A Few Overview Readings (I)
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose,
Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey”
IEEE Micro, August 2020.
https://arxiv.org/pdf/2008.00961.pdf

## Slide 7: A Few Overview Readings (II)
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]
https://arxiv.org/pdf/2106.06433.pdf

## Slide 8: A Few Overview Readings (III)
Mohammed Alser, Joel Lindegger, Can Firtina, Nour Almadhoun, Haiyu Mao, Gagandeep Singh, Juan Gomez-Luna, Onur Mutlu
“From Molecules to Genomic Variations: Intelligent Algorithms and Architectures for Intelligent Genome Analysis”
Computational and Structural Biotechnology Journal, 2022
[Source code]
https://arxiv.org/pdf/2205.07957.pdf

## Slide 9: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 10: What Is a Genome Made Of?
Cell
Nucleus
The discovery of DNA’s double-helical structure (Watson+, 1953)
Notes: Unlocking the life’s code requires diving into the nucleus of our body cells, where the double-stranded genome resides. Genome is literally the 'code of life' - it is the set of instructions for making everything from you to zebras, strawberries, and even yeast.
since the discovery of dna’s double-helical structure (watson et al. 1953)

## Slide 11: The Central Dogma of Molecular Biology
Phenotypes
Genotypes
Notes: Our DNA is literally a cookbook that contains the information needed to make all of our phenotypes and traits. Our genes are the recipes for making us what we are physically.

## Slide 12: DNA Under Electron Microscope
human chromosome #12
from HeLa’s cell
Notes: Henrietta Lacks,

## Slide 13
CCTCCTCAGTGCCACCCAGCCCACTGGCAGCTCCCAAACAGGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTGAGGTGTCAAGGACCTAAACTAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTGCTAAACAGCACTTTTTTGACCATTATTTTGGATCTGAAAGAAATCAAGAATAAATGAAGGACTTGATACATTGGAAGAGGAGAGTCAAGGACCTACAGAAAAAAAAAAAAAAGAAAAAGAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCTGTGTTGCAGGTCTTCTTGCATTTCCCTGTCAAAAGAAAAAGAATTTAAAATTTAAGTAATTCTTTGAAAAAAACTAATTTCTAAGCTTCTTCATGTCAAGGACCTAATGTCAGGCC
GGCTCTTATTAAAACACCCTGTTCCCTGCCCCTTGGAGTG

## Slide 14: How Large is a Genome?
Phi X174 virus
5.386 Kilo bp
E. coli O157:H7
5.44 Million bp
Homo Sapiens
3.2 Billion bp
Onion, Allium Cepa
16 Billion bp
Paris Japonica
149 Billion bp
Notes: Phi x174 is a virus that Infects E. Coli bacteria
You may be exposed to E. coli from contaminated water or food — especially raw vegetables and undercooked ground beef.
Paris Japonica : A rare Japanese flower
============================
Phi is 600K time smaller than the genome of human
E coli is ~600 time smaller than the human genome
Onion has a genome that is 5x larger than that of human
Paris japonica’s genome is 46x larger than the human genome

## Slide 15: DNA Sequencing
Goal:
  Find the complete sequence of A, C, G, T’s in an organism’s DNA
Challenge:
  There is no machine that takes long DNA as an input, and gives the complete sequence as output
  All sequencing machines chop DNA into pieces and identify relatively small pieces (but not how they fit together)

## Slide 16: Genome Sequencing
Large DNA molecule
Small DNA fragments
Reads
ACGTACCCCGT
GATACACTGTG
TTTTTTTAATT
CTAGGGACCTT
ACGACGTAGCT
AAAAAAAAAA
ACGAGCGGGT
Notes: As the whole genome of most organisms cannot be sequenced all at once, the genome is broken into smaller fragments.
After each fragment is sequenced, small pieces of DNA sequences (i.e. reads) are generated.

## Slide 17: Genome Sequencing and Analysis
Current sequencing machines provide
small randomized fragments
of the original DNA sequence
Alser+, "Technology dictates algorithms: Recent developments in read alignment", Genome Biology, 2021
Read Mapping
Reads

## Slide 18: Untangling Yarn Balls & DNA Sequencing
Notes: untangling yarn ball

## Slide 19
Genome Sequencers
… and more! All produce data with different properties.
Roche/454
Illumina HiSeq2000
Ion Torrent PGM
Ion Torrent Proton
AB SOLiD
Oxford Nanopore GridION
Oxford Nanopore MinION
Complete
Genomics
Illumina MiSeq
Pacific Biosciences RS
Illumina
NovaSeq
6000

## Slide 20: High-Throughput Sequencers
… and more! All produce data with different properties.
Illumina MiSeq
Oxford Nanopore MinION
Pacific Biosciences RS II
Illumina NovaSeq 6000
Oxford
Nanopore SmidgION
Pacific
Biosciences
Sequel II
Oxford
Nanopore
PromethION

## Slide 21: The Genomic Era
development of high-throughput sequencing (HTS) technologies
http://www.economist.com/news/21631808-so-much-genetic-data-so-many-uses-genes-unzipped
Number of Genomes Sequenced
Notes: However, since the development of high throughput sequencing (HTS) technologies, the cost of genome sequencing has fallen off a cliff (<< 1,000$) making it viable for almost everyone's use.

## Slide 22: Genome Sequencing Cost Is Reducing
*From NIH (https://www.genome.gov/about-genomics/fact-sheets/DNA-Sequencing-Costs-Data)

## Slide 23: Genome Sequencing Cost Is Reducing
*From NIH (https://www.genome.gov/about-genomics/fact-sheets/DNA-Sequencing-Costs-Data)

## Slide 24: Solving the Puzzle
https://www.pacb.com/smrt-science/smrt-sequencing/hifi-reads-for-highly-accurate-long-read-sequencing/
Sequenced Reads
Reference genome
.FASTA file
.FASTQ file
Notes: Rhinoceros

## Slide 25: Newer Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version] [Slides (pptx) (pdf)] [Talk Video at AACBB 2019]
Oxford Nanopore MinION

## Slide 26: Types of Genomic Reads
Wenger+, "Accurate circular consensus long-read sequencing improves variant detection and assembly of a human genome", Nature Biotechnology, 2019
But still very expensive!
https://labs.wsu.edu/genomicscore/illumina-sequencing/
https://pacbio.gs.washington.edu/
Long: 10-20 kb
Accurate: 99.8%
Notes: By sequencing the same DNA segment many times (10 to 30 times), we can have accurate more longer reads.

## Slide 27
Genome Analysis
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
Notes: Genome analysis starts with sequencing random short DNA fragments of copies of the original molecule.
Unfortunately, these reads lack information about their order and which part of genome they are originated from.
Hence the second step is to map these reads to a long reference genome.

## Slide 28: Read Mapping Techniques in 111 Pages
Mohammed Alser, Jeremy Rotman, Dhrithi Deshpande, Kodi Taraszka, Huwenbo Shi, Pelin Icer Baykal, Harry Taegyun Yang, Victor Xue, Sergey Knyazev, Benjamin D. Singer, Brunilda Balliu, David Koslicki, Pavel Skums, Alex Zelikovsky,
Can Alkan, Onur Mutlu, Serghei Mangul
"Technology dictates algorithms: Recent developments in read alignment"
Genome Biology, 2021
[Source code]
In-depth analysis of 107 read mappers (1988-2020)

## Slide 29: One Problem

## Slide 30
1
2
Sequencing
Read Mapping
3
4
Variant Calling
Scientific Discovery
300 M
bases/min
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Illumina HiSeq4000
2 M
bases/min
on average
(0.6%)
We Are Bottlenecked in Read Mapping
Notes: Typical sequencer machine generates a flood of reads, for example, Illumina HiSeq4000 generates 300 million bases/minute.
However, existing computer alignment algorithms can only process 0.6% of these reads in the same amount of time.
This gap is widening as more advanced sequencers are made available in the market.

## Slide 31: The Read Mapping Bottleneck
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Read Sequencing
Read Mapping
* BWA-MEM
** HiSeqX10, MinION
*
**
150x slower
Million
bases/minute
300
Million
bases/minute
2
Notes: 12.48
5.2 CPU hours
144x
60 CPU hours
BWA-MEM
25 minutes
Illumine HiSeq X10
25 minutes
Nanopore MinION
Short reads generated in a day using today’s HTS machines (e.g., Illumine HiSeq X10) can be mapped to the human reference genome using BWA-MEM [36], a popular and widely-used read mapper, in 12.5 CPU (central processing unit) days when running on a single core [66, 67]. BWA-MEM also takes about 2.5 CPU days to map long reads that are generated in 25 minutes using today’s Nanopore MinION sequencer [68]

## Slide 32: The Read Mapping Bottleneck
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
GAGTCAGAATTTGAC
Human whole
genomes
Human
1
Illumina NovaSeq 6000
48
at 30× coverage
in about 2 days
genome
32 CPU hours
on a 48-core processor
Chart: 
| Read Mapping | Others
Sales | 0.71 | 0.29
Goyal+, "Ultra-fast next generation human genome sequencing data processing using DRAGENTM bio-IT processor for precision medicine”, Open Journal of Genetics, 2017.
Notes: 12.48
5.2 CPU hours
144x
60 CPU hours
BWA-MEM
25 minutes
Illumine HiSeq X10
25 minutes
Nanopore MinION
Short reads generated in a day using today’s HTS machines (e.g., Illumine HiSeq X10) can be mapped to the human reference genome using BWA-MEM [36], a popular and widely-used read mapper, in 12.5 CPU (central processing unit) days when running on a single core [66, 67]. BWA-MEM also takes about 2.5 CPU days to map long reads that are generated in 25 minutes using today’s Nanopore MinION sequencer [68]

## Slide 33: Problem with (Genome) Analysis Today
Special-Purpose Machine
for Data Generation
General-Purpose Machine
for Data Analysis
FAST SLOW
Slow and inefficient processing capability
This picture is similar for many “data generators & analyzers” today

## Slide 34: One Problem
Need to construct
the entire genome
from many sequenced reads

## Slide 35: Read Mapping
Map many short DNA fragments (reads) to a known reference genome with some differences allowed
Reference genome
Reads
DNA, logically
DNA, physically
Mapping short reads to reference genome is challenging (billions of 50-300 base pair reads)
Notes: Read mapping is a post processing procedure after DNA sequencing. It maps the data output from a DNA sequencer, which are many short DNA fragments, to a known reference genome, with some minor differences allowed.
To illustrate the problem better, let us take a closer look at the DNA itself. Logically, the DNA is a double stranded long string. In reality, within a cell they folded into a sphere in the nucleus like a ball of wool. Since it is very hard to disentangle the DNA at molecular level, to extract the information out, a sequencer cuts the mass into many short DNA pieces which are called reads.
A mapper’s job is to find where these DNA short reads are most likely to be originally placed so that later we can assemble them in the correct order to restore the original DNA.
Mapping these short reads, up to billions of them, with each one being 50 to 300 base-pairs long, to the reference genome is challenging.

## Slide 36: Read Mapping for Metagenomic Analysis
Reference Database
Reads in
“text format”
Genetic material recovered directly from environmental samples
Reads from different unknown donors at sequencing time are mapped to many known reference genomes
Notes: Read mapping is a post processing procedure after DNA sequencing. It maps the data output from a DNA sequencer, which are many short DNA fragments, to a known reference genome, with some minor differences allowed.
To illustrate the problem better, let us take a closer look at the DNA itself. Logically, the DNA is a double stranded long string. In reality, within a cell they folded into a sphere in the nucleus like a ball of wool. Since it is very hard to disentangle the DNA at molecular level, to extract the information out, a sequencer cuts the mass into many short DNA pieces which are called reads.
A mapper’s job is to find where these DNA short reads are most likely to be originally placed so that later we can assemble them in the correct order to restore the original DNA.
Mapping these short reads, up to billions of them, with each one being 50 to 300 base-pairs long, to the reference genome is challenging.

## Slide 37: Computational Cost is Mathematically Proven
https://arxiv.org/abs/1412.0348

## Slide 38: Read Mapping Techniques in 111 Pages
Mohammed Alser, Jeremy Rotman, Dhrithi Deshpande, Kodi Taraszka, Huwenbo Shi, Pelin Icer Baykal, Harry Taegyun Yang, Victor Xue, Sergey Knyazev, Benjamin D. Singer, Brunilda Balliu, David Koslicki, Pavel Skums, Alex Zelikovsky,
Can Alkan, Onur Mutlu, Serghei Mangul
"Technology dictates algorithms: Recent developments in read alignment"
Genome Biology, 2021
[Source code]
In-depth analysis of 107 read mappers (1988-2020)

## Slide 39: Read Mapping Execution Time (Modern)
ONT FASTQ size: 103MB (151 reads), Mean length: 356,403 bp, std: 173,168 bp, longest length: 817,917 bp
Chart: 
| KSW2 | Seed Chaining | Sorting Seeds | Collect Matching Seeds | Collect Minimizers
Sales | 0.46 | 0.16 | 0.29 | 0.08 | 0.02
>60%
of the read mapper’s execution time is spent in sequence alignment
minimap2

## Slide 40: Accelerating Read Mapping
Alser+, “Accelerating Genome Analysis: A Primer on an Ongoing Journey”, IEEE Micro, 2020.

## Slide 41: Detailed Analysis of Tackling the Bottleneck
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose,
Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey”
IEEE Micro, August 2020.

## Slide 42: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 43: GateKeeper: FPGA-Based Alignment Filtering
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 44: GateKeeper Accelerator Architecture
Maximum data throughput =~13.3 billion bases/sec
Can examine 8 (300 bp) or 16 (100 bp) mappings concurrently at 250 MHz
Occupies 50% (100 bp) to 91% (300 bp) of the FPGA slice LUTs and registers
Notes: Here, we present the architecture of GateKeeper. Each processing core is able to examine a single mapping in a single clock cycle. We integrate many hardware processing cores in the architecture of GateKeeper for examining many mappings in a parallel fashion. The input read-reference pairs are transferred from the host to the FPGA via PCIe third generation 4-lane at the rate of 13.3 billion bases/sec. With this data throughput, we can have 16 processing cores work concurrently to examine 16 read-reference pairs. Our architecture occupies only 50% of the FPGA resource for a read length of 100 bp and 91% for a read length of 300 bp.

## Slide 45: FPGA Chip Layout
Read length:
300 bp
Error threshold:
E=15

## Slide 46: GateKeeper: Speed & Accuracy Results
90x-130x faster filter
than SHD (Xin et al., 2015) and the Adjacency Filter (Xin et al., 2013)
4x lower false accept rate
than the Adjacency Filter (Xin et al., 2013)
10x speedup in read mapping
with the addition of GateKeeper to the mrFAST mapper (Alkan et al., 2009)
Freely available online github.com/BilkentCompGen/GateKeeper

## Slide 47: GateKeeper Conclusions
FPGA-based pre-alignment greatly speeds up read mapping
  10x speedup of a state-of-the-art mapper (mrFAST)
FPGA-based pre-alignment can be integrated with the sequencer
  It can help to hide the complexity and details of the FPGA
  Enables real-time filtering while sequencing
  Paves the way to on-device genome analysis

## Slide 48: More on GateKeeper
Mohammed Alser, Hasan Hassan, Hongyi Xin, Oguz Ergin, Onur Mutlu, and Can Alkan "GateKeeper: A New Hardware Architecture for Accelerating Pre-Alignment in DNA Short Read Mapping" Bioinformatics, [published online, May 31], 2017. [Source Code] [Online link at Bioinformatics Journal]

## Slide 49: Algorithm-Arch-Device Co-Design is Critical
Micro-architecture
SW/HW Interface
Program/Language
Algorithm
Problem
Logic
Devices
System Software
Electrons
Computer Architecture (expanded view)

## Slide 50: Shouji (障子) [Alser+, Bioinformatics 2019]
Mohammed Alser, Hasan Hassan, Akash Kumar, Onur Mutlu, and Can Alkan, "Shouji: A Fast and Efficient Pre-Alignment Filter for Sequence Alignment" Bioinformatics, [published online, March 28], 2019. [Source Code] [Online link at Bioinformatics Journal]

## Slide 51: Hardware Implementation
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
Counting is performed concurrently for all bit-vectors and
all sliding windows in a single clock cycle using multiple 4-input LUTs

## Slide 52: SneakySnake [Alser+, Bioinformatics 2020]
Mohammed Alser, Taha Shahroodi, Juan-Gomez Luna, Can Alkan, and Onur Mutlu, "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs" Bioinformatics, to appear in 2020. [Source Code] [Online link at Bioinformatics Journal]

## Slide 53: SneakySnake
Key observation:
  Correct alignment is a sequence of non-overlapping long matches
Key idea:
  Reduce the approximate string matching problem to the Single Net Routing problem in VLSI chip layout
VLSI chip layout

## Slide 54: More on SneakySnake [Alser+, Bioinformatics 2020]
Mohammed Alser, Taha Shahroodi, Juan-Gomez Luna, Can Alkan, and Onur Mutlu, "SneakySnake: A Fast and Accurate Universal Genome Pre-Alignment Filter for CPUs, GPUs, and FPGAs" Bioinformatics, to appear in 2020. [Source Code] [Online link at Bioinformatics Journal]

## Slide 55: GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 56: GenASM: ASM Framework for GSA
GenASM: First ASM acceleration framework for GSA
  Based on the Bitap algorithm
    Uses fast and simple bitwise operations to perform ASM
  Modified and extended ASM algorithm
    Highly-parallel Bitap with long read support
    Bitvector-based novel algorithm to perform traceback
  Co-design of our modified scalable and memory-efficient algorithms with low-power and area-efficient hardware accelerators
Our Goal:
Accelerate approximate string matching
by designing a fast and flexible framework,
which can accelerate multiple steps of genome sequence analysis
Notes: [CLICK] Our goal in this work is to design a fast and flexible framework for both short and long reads, which can accelerate multiple steps of genome sequence analysis (GSA).
[CLICK] To this end, we propose GenASM
[CLICK] We base GenASM on Bitap, an ASM algorithm that uses only fast and simple bitwise operations, making it amenable to efficient hardware acceleration. To our knowledge, GenASM is the first work that enhances and accelerates Bitap, and also it is the first ASM acceleration framework for genome sequence analysis.
[CLICK] We modify Bitap to support long reads and to enable parallelization.
We also develop a novel Bitap-compatible algorithm for traceback, which uses information collected during ASM about the different types of errors to identify the optimal alignment of reads.
[CLICK] And, we co-design specialized, low-power and area-efficient hardware for both algorithms.

## Slide 57: GenASM: Hardware Design
GenASM-DC
GenASM-TB
GenASM-DC:
generates bitvectors
and performs edit
Distance Calculation
GenASM-TB: performs TraceBack and assembles the optimal alignment
Host CPU
TB-SRAM1
TB-SRAM2
TB-SRAMn
GenASM-TB
Accelerator
GenASM-DC
Accelerator
GenASM-TB
Accelerator
GenASM-DC
Accelerator
Main Memory
DC-SRAM
DC-SRAM
GenASM-DC
GenASM-TB
TB-SRAM1
TB-SRAM2
TB-SRAMn
.
.
.
Notes: Our co-designed hardware consists of two components:
(1) GenASM-DC, which provides hardware support to efficiently execute our modified Bitap algorithm to perform distance calculation; and
(2) GenASM-TB, which provides hardware support to efficiently execute our novel traceback algorithm to find the optimal alignment.
GenASM also has two types of SRAM buffers:
DC-SRAM, and
TB-SRAMs

## Slide 58: Key Results – Area and Power
Based on our synthesis of GenASM-DC and GenASM-TB accelerator datapaths using the Synopsys Design Compiler with a 28nm LP process:
  Both GenASM-DC and GenASM-TB operate @ 1GHz
  Total (1 vault): 0.334 mm2 0.101 W
  Total (32 vaults): 10.69 mm2 3.23 W
  % of a Xeon CPU core: 1% 1%
Notes: [CLICK] We synthesize our DC and TB accelerator datapaths with a typical 28nm low-power process:
[CLICK] Both accelerators operates at 1GHz.
[CLICK] We find that for 32 GenASM accelerator (one for each HMC vault), total area overhead is ten point sixty nine millimeter square and total power consumption is three point twenty-three watts.
We observe that both area and power consumption of GenASM (at 1 vault) is around 1% of the area and power consumption of a single Xeon CPU core.

## Slide 59: Key Results – Area and Power
Based on our synthesis of GenASM-DC and GenASM-TB accelerator datapaths using the Synopsys Design Compiler with a 28nm LP process:
  Both GenASM-DC and GenASM-TB operate @ 1GHz
  GenASM has low area and power overheads
Notes: Thus, GenASM has low area and power overheads.

## Slide 60: Use Cases of GenASM
Indexing
Seeding
Pre-Alignment Filtering
Read Alignment
Reference genome
Hash table based index
Candidate mapping locations
Optimal alignment
Reads from sequenced genome
Remaining candidate mapping locations
Indexing
Seeding
Notes: GenASM is flexible and can be used for a number of use cases.
In this work, we evaluate three of them in detail and two of them are from the read mapping pipeline:
Pre-alignment filtering and read alignment

## Slide 61: Key Results
Read Alignment
116× speedup, 37× less power than Minimap2 (state-of-the-art SW)
111× speedup, 33× less power than BWA-MEM (state-of-the-art SW)
3.9× better throughput, 2.7× less power than Darwin (state-of-the-art HW)
1.9× better throughput, 82% less logic power than GenAx (state-of-the-art HW)
Pre-Alignment Filtering
3.7× speedup, 1.7× less power than Shouji (state-of-the-art HW)
Edit Distance Calculation
22–12501× speedup, 548–582× less power than Edlib (state-of-the-art SW)
9.3–400× speedup, 67× less power than ASAP (state-of-the-art HW)
Notes: We find that, for all the three use cases, GenASM is significantly more efficient in terms of both speed and power consumption than state-of-the-art software and hardware baselines

## Slide 62: More on GenASM Framework [MICRO 2020]
Damla Senol Cali, Gurpreet S. Kalsi, Zulal Bingol, Can Firtina, Lavanya Subramanian, Jeremie S. Kim, Rachata Ausavarungnirun, Mohammed Alser, Juan Gomez-Luna, Amirali Boroumand, Anant Nori, Allison Scibisz, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "GenASM: A High-Performance, Low-Power Approximate String Matching Acceleration Framework for Genome Sequence Analysis" Proceedings of the 53rd International Symposium on Microarchitecture (MICRO), Virtual, October 2020. [Lighting Talk Video (1.5 minutes)] [Lightning Talk Slides (pptx) (pdf)] [Talk Video (18 minutes)] [Slides (pptx) (pdf)]

## Slide 63: Accelerating Sequence-to-Graph Mapping
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 64: Genome Sequence Analysis
Sequence-to-Sequence (S2S) Mapping
Sequence-to-Graph (S2G) Mapping
Sequence-to-graph mapping results in notable quality improvements.
However, it is a more difficult computational problem,
with no prior hardware design.
Mapping the reads to a reference genome (i.e., read mapping) is a critical step in genome sequence analysis
Linear Reference: ACGTACGT
Read: ACGG
Alternative Sequence: ACGGACGT
Alternative Sequence: ACGTTACGT
Alternative Sequence: ACG‒ACGT
Graph-based Reference:
Read: ACGG
Notes: Read mapping, which is the process of mapping the reads to a reference genome is a critical step in genome sequence analysis
Traditionally, we perform seq2seq mapping, where we
Map reads collected from an individual to a known linear reference genome sequence
Emphasizes the genetic variations that are present in the single reference genome
Ignores other variations that are not represented in the single linear reference sequence
Introduces reference bias
However, s2s mapping is a well studied problem with many available tools and accelerators
Recent works replace the linear reference sequence with a graph-based representation of the reference genome (genome graph). Thus, we can perform seq2graph mapping.
Captures the genetic variations and diversity across many individuals in a population
[CLICK] Results in notable quality improvements in GSA

## Slide 65: SeGraM: First Graph Mapping Accelerator
SeGraM: First universal algorithm/hardware co-designed genomic mapping accelerator that can effectively and efficiently support:
Sequence-to-graph mapping
Sequence-to-sequence mapping
Both short and long reads
Our Goal:
Specialized, high-performance, scalable, and low-cost algorithm/hardware co-design that alleviates bottlenecks in multiple steps of sequence-to-graph mapping
Notes: [CLICK] Thus, our goal is to come up with a specialized, high-performance, scalable, and low-cost algorithm/hardware co-design that alleviates bottlenecks in both the seeding and alignment steps of sequence-to-graph mapping.
[CLICK] To this end, we propose SeGraM, a universal algorithm/hardware co-designed genomic mapping accelerator that can effectively and efficiently support both sequence-to-graph mapping and sequence-to-sequence mapping, for both short and long reads. To our knowledge, SeGraM is the first algorithm/hardware co-design for accelerating
sequence-to-graph mapping.

## Slide 66: Sequence-to-Graph Mapping Pipeline
Pre-Processing
Steps (Offline)
Seed-and-Extend
Steps (Online)
Indexing
(index the nodes of the graph)
Seeding
(query the index & find the seed matches)
Filtering/Chaining/Clustering
(filter out dissimilar query read and subgraph pairs)
S2G Alignment
(perform distance/score calculation & traceback)
Linear reference genome
Known genetic variations
Reads from sequenced
genome
0.2
1
2
3
Genome Graph Construction
(construct the graph using a linear reference genome and variations)
0.1
Genome graph
Hash-table-based index (of graph nodes)
Candidate mapping locations (subgraphs)
Remaining candidate mapping locations (subgraphs)
Optimal alignment between read & subgraph
Notes: Which brings us to seq2graph mapping.
Sequence-to-graph mapping pipeline has [CLICK] two pre-processing and [CLICK] three main steps.
[CLICK] The first pre-processing step constructs the genome graph using a linear reference genome and the associated variations for that genome.
[CLICK] The second pre-processing step indexes the nodes of the graph. The resulting index is used in the first main step of the pipeline, [CLICK] seeding, which aims to find seed matches between the query read and a region of the graph.
[CLICK] After optionally filtering these seed matches with a filtering, chaining, or clustering step, [CLICK] alignment is performed between all of the non-filtered seed locations within the graph and the query read to find the optimal alignment. Alignment is the most expensive step of the pipeline, so let’s look at it in detail.

## Slide 67: Use Cases & Key Results
Sequence-to-Graph (S2G) Mapping
5.9×/106× speedup, 4.1×/3.0× less power than GraphAligner for long and short reads, respectively (state-of-the-art SW)
3.9×/742× speedup, 4.4×/3.2× less power than vg for long and short reads, respectively (state-of-the-art SW)
Sequence-to-Graph (S2G) Alignment
41×–539× speedup over PaSGAL with AVX-512 support (state-of-the-art SW)
Sequence-to-Sequence (S2S) Alignment
1.2×/4.8× higher throughput than GenASM and GACT of Darwin for long reads (state-of-the-art HW)
1.3×/2.4× higher throughput than GenASM and SillaX of GenAX for short reads (state-of-the-art HW)
Notes: [CLICK] [CLICK] [CLICK] We demonstrate that SeGraM provides significant improvements for multiple steps of the sequence-to-graph (i.e., S2G) and sequence-to-sequence (i.e., S2S) mapping pipelines.
==================================================================================================================
[CLICK] We show that (1) SeGraM provides greatly higher throughput and lower power consumption on both short and long reads compared to state-of-the-art software tools for sequence-to-graph mapping, and
[CLICK] (2) BitAlign significantly outperforms a state-of-the-art sequence-to-graph alignment tool and [CLICK] three state-of-the-art hardware solutions that are specifically designed for sequence-to-sequence alignment.
===========================================================================================================
We also show that MinSeed can be employed for the seeding step of both sequence-to-graph and sequence-to-sequence mapping pipelines.

## Slide 68: SeGraM Talk Video
https://www.youtube.com/watch?v=gyjqYoyDP9s

## Slide 69: Accelerating Sequence-to-Graph Mapping
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 70: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 71: Read Mapping & Filtering in Memory
We need to design
mapping & filtering algorithms
that fit processing-in-memory

## Slide 72: Near-Memory Pre-Alignment Filtering
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]

## Slide 73: Near-Memory Acceleration using FPGAs
IBM POWER9 CPU
HBM-based FPGA board
OCAPI
Source: AlphaData
Source: IBM
Near-HBM FPGA-based accelerator
Two communication technologies: CAPI2 and OCAPI
Two memory technologies: DDR4 and HBM
Two workloads: Weather Modeling and Genome Analysis
Notes: To this end we build a [CLICK] near-HBM FPGA based accelerator which is connected to a server-grade IBM POWER9-based CPU system

## Slide 74: Performance & Energy Greatly Improve
5-27× performance vs. a 16-core (64-thread) IBM POWER9 CPU
HBM alleviates memory bandwidth contention vs. DDR4
12-133× energy efficiency vs. a 16-core (64-thread) IBM POWER9 CPU
Notes: [CLICK]

## Slide 75: More On Near-Memory SneakySnake
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]

## Slide 76: In-Storage Genome Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 77: Genome Sequence Analysis
Computation overhead
Data movement overhead
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Alignment
Data Movement from Storage
Storage
System
Notes: Read mapping performs alignment on large genomic datasets, containing millions of reads. [CLICK]
Therefore, read mapping is both computationally expensive [CLICK]
And incurs high data movement overhead [CLICK]

## Slide 78: Accelerating Genome Sequence Analysis
Heuristics
Accelerators
Filters
Computation overhead
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Data movement overhead
✓
Notes: There has been significant effort into improving read mapping performance [CLICK]
Through efficient heuristics [CLICK]
hardware accelerators [CLICK]
and various filters that prune reads that do not require expensive computation [CLICK].
While these approaches address the computation overhead in read mapping [CLICK]
[While Reads Move] None of them alleviate the data movement overhead from storage, whose impact becomes even larger when the computation overhead gets alleviated [CLICK]

## Slide 79: Key Idea
Storage
System
Non-matching reads
Do not have potential matching locations and can skip alignment
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Notes: Our key idea is to filter reads that do not require the expensive alignment computation in the storage system [CLICK] …
[While Reads Move] To fundamentally reduce the data movement overhead of read mapping
Examples of the reads that not require the costlt alignment step
Exactly-matching reads to the reference genome that do not need approximate string matching performed during alignment
Non-matching reads that have no potential matching locations in the reference genome hence skip the alignemt step

## Slide 80: Filtering Opportunities
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate and short
  Long reads: less accurate and long
High sequencing error rates (long reads) or
High genetic variation (short or long reads)
Non-matching reads
Do not have potential matching locations, so they skip alignment
Low sequencing error rates (short reads) combined with
Low genetic variation
Exactly-matching reads
Do not need expensive approximate string matching during alignment
Reads that do not require the expensive alignment step:
Notes: Let’s take a look at filtering opportunities based on the input reads.
Sequencing machines produce one of two kinds of reads
  Short reads: highly accurate (99.9%) and short (e.g., up to a few hundreds of DNA characters)
  Long reads: less accurate (85-90%) and long (e.g., from hundreds to millions of DNA characters)
Based on these, We leverage two filtering opportunities
First, we can filter exactly matching reads, which are reads that match exactly to one or more subsequences of the reference genome and do not require approximate string matching during alignment. Exact matches can frequently occur in short read sets with low sequencing errors and low genetic variations
Second, we can filter non-matching reads. Such reads do not have any potential matching locations in the reference genome can skip the expensive alignment step. Non-matching reads can frequently occur in long read sets with high sequencing errors and short or long read sets with high genetic variations

## Slide 81: Challenges
Read mapping workloads can exhibit different behavior
There are limited hardware resources
in the storage system
Filter reads that do not require alignment
inside the storage system
AAGCTTCCATGG
AAAATTCCATGG
TTTTTTCCAAAA
GCTTCCAGAATG
GGGCCAGAATG
GAATGGGGCCA
TCCCCGGGGCCA
CCTTTGGGTCCA
CGTTCCTTGGCA
Filtered Reads
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
Storage
System
Notes: However, filtering reads in a modern SSD can be challenging [CLICK]
Due to different behavior across read mapping workloads. [CLICK]
And the limited hardware resources in the SSD. By addressing these challenges [CLICK]

## Slide 82: GenStore
Computation overhead
Data movement overhead
  GenStore provides significant speedup (1.4x - 33.6x) and
  energy reduction (3.9x – 29.2x) at low cost
Filter reads that do not require alignment
inside the storage system
Computation
Unit
(CPU or Accelerator)
Cache
Main
Memory
GenStore-Enabled
Storage
System
✓
✓
Notes: We propose GenStore, the first in-storage processing system designed for genome sequence analysis. [CLICK]
To reduce both the computation [CLICK]
And the data movement overhead [CLICK]
GenStore provides high-performance and energy benefits compared to state-of-the-art HW and SW baselines [CLICK]

## Slide 83: In-Storage Genome Filtering [ASPLOS 2022]
Nika Mansouri Ghiasi, Jisung Park, Harun Mustafa, Jeremie Kim, Ataberk Olgun, Arvid Gollwitzer, Damla Senol Cali, Can Firtina, Haiyu Mao, Nour Almadhoun Alserr, Rachata Ausavarungnirun, Nandita Vijaykumar, Mohammed Alser, and Onur Mutlu, "GenStore: A High-Performance and Energy-Efficient In-Storage Computing System for Genome Sequence Analysis" Proceedings of the 27th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS), Virtual, February-March 2022. [Lightning Talk Slides (pptx) (pdf)] [Lightning Talk Video (90 seconds)]

## Slide 84: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/1903.03988.pdf

## Slide 85: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 86: More on Processing-in-Memory
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 87: A Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=H3sEaINPBOE

## Slide 88: Processing-in-Memory Landscape Today
[UPMEM 2019]
[Samsung 2021]
[SK Hynix 2022]
[Samsung 2021]
This does not include many experimental chips and startups
[Alibaba 2022]

## Slide 89: UPMEM Processing-in-DRAM Engine (2019)
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/

## Slide 90: UPMEM Memory Modules
E19: 8 chips DIMM (1 rank). DPUs @ 267 MHz
P21: 16 chips DIMM (2 ranks). DPUs @ 350 MHz
www.upmem.com

## Slide 91: 2,560-DPU Processing-in-Memory System
https://arxiv.org/pdf/2105.03814.pdf

## Slide 92: More on the UPMEM PIM System
https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=26

## Slide 93: AIM (PIM Sequence Alignment Framework)
Safaa Diab, Amir Nassereldine, Mohammed Alser, Juan Gómez-Luna,
Onur Mutlu, Izzat El Hajj
“A Framework for High-throughput Sequence Alignment using Real Processing-in-Memory Systems“
arXiv, 2022
[Source code]

## Slide 94: Accelerating Genome Analysis w/ Processing using NVM
Appears at MICRO 2022
https://arxiv.org/pdf/2209.08600.pdf

## Slide 95: Agenda
The Problem: DNA Read Mapping
  State-of-the-art Read Mapper Design
Algorithmic Acceleration
  Exploiting Structure of the Genome
  Exploiting SIMD Instructions
Hardware Acceleration
  Specialized Architectures
  Processing in Memory & Storage
Future Opportunities: New Technologies & Applications

## Slide 96: Newer Genome Sequencing Technologies
Senol Cali+, “Nanopore Sequencing Technology and Tools for Genome
Assembly: Computational Analysis of the Current State, Bottlenecks
and Future Directions,” Briefings in Bioinformatics, 2018.
[Open arxiv.org version] [Slides (pptx) (pdf)] [Talk Video at AACBB 2019]
Oxford Nanopore MinION

## Slide 97: New Applications: Graph Genomes
Damla Senol Cali, Konstantinos Kanellopoulos, Joel Lindegger, Zulal Bingol, Gurpreet S. Kalsi, Ziyi Zuo, Can Firtina, Meryem Banu Cavlak, Jeremie Kim, Nika MansouriGhiasi, Gagandeep Singh, Juan Gomez-Luna, Nour Almadhoun Alserr, Mohammed Alser, Sreenivas Subramoney, Can Alkan, Saugata Ghose, and Onur Mutlu, "SeGraM: A Universal Hardware Accelerator for Genomic Sequence-to-Graph and Sequence-to-Sequence Mapping" Proceedings of the 49th International Symposium on Computer Architecture (ISCA), New York, June 2022. [arXiv version]
https://arxiv.org/pdf/2205.05883.pdf

## Slide 98: New Applications: Ref Genome Updates
https://people.inf.ethz.ch/omutlu/pub/AirLift_genome-remapper_arxiv21.pdf

## Slide 99: Remapping Reads Between References
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Nastaran Hajinazar, Mohammed Alser, Can Alkan, and Onur Mutlu, "AirLift: A Fast and Comprehensive Technique for Remapping Alignments between Reference Genomes" Preprint in arXiv and bioRxiv, 2021. [bioRxiv preprint] [arXiv preprint] [AirLift Source Code and Data]

## Slide 100: Mapping Constant Regions Between References
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Can Alkan, and Onur Mutlu, "FastRemap: A Tool for Quickly Remapping Reads between Genome Assemblies" Bioinformatics, btac554. [FastRemap Source Code]

## Slide 101: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 102: Conclusion

## Slide 103: Things Are Happening In Industry

## Slide 104: Illumina DRAGEN Bio-IT Platform (2018)
Processes whole genome at 30x coverage in ~25 minutes with hardware support for data compression
FPGA board(s)
emea.illumina.com/products/by-type/informatics-products/dragen-bio-it-platform.html
emea.illumina.com/company/news-center/press-releases/2018/2349147.html

## Slide 105: NVIDIA Clara Parabricks (2020)
https://developer.nvidia.com/clara-parabricks
GPU board(s)
A University of Michigan startup in 2018 joined NVIDIA in 2020

## Slide 106: NVIDIA Hopper DPX Instructions (2022)
https://blogs.nvidia.com/blog/2022/03/22/nvidia-hopper-accelerates-dynamic-programming-using-dpx-instructions/

## Slide 107: Recall Our Dream (from 2007)
An embedded device that can perform comprehensive genome analysis in real time (within a minute)
Still a long ways to go
  Energy efficiency
  Performance (latency)
  Security & privacy
  Huge memory bottleneck

## Slide 108: Conclusion
System design for bioinformatics is a critical problem
  It has large scientific, medical, societal, personal implications
This talk is about accelerating a key step in bioinformatics: genome sequence analysis
  In particular, read mapping
We covered various recent ideas to accelerate read mapping
  My personal journey since September 2006
Many future opportunities exist
  Especially with new sequencing technologies
  Especially with new applications and use cases

## Slide 109: A Bright Future for Intelligent Genome Analysis
SmidgION from ONT
MinION from ONT
Mohammed Alser, Zülal Bingöl, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, Onur Mutlu
“Accelerating Genome Analysis: A Primer on an Ongoing Journey” IEEE Micro, August 2020.

## Slide 110: A Longer Version of This Talk
https://www.youtube.com/watch?v=NCagwf0ivT0

## Slide 111: Accelerating Genome Analysis A Primer on an Ongoing Journey
Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
3 November 2022
Montenegro Academy of Sciences Conference

## Slide 112: Backup Slides for Further Info

## Slide 113: Resources & Acknowledgments

## Slide 114: Accelerating Genome Analysis: Overview
Mohammed Alser, Zulal Bingol, Damla Senol Cali, Jeremie Kim, Saugata Ghose, Can Alkan, and Onur Mutlu, "Accelerating Genome Analysis: A Primer on an Ongoing Journey" IEEE Micro (IEEE MICRO), Vol. 40, No. 5, pages 65-75, September/October 2020. [Slides (pptx)(pdf)] [Talk Video (1 hour 2 minutes)]

## Slide 115: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, to be published in 2021.
https://arxiv.org/pdf/2012.03112.pdf

## Slide 116: PIM Review and Open Problems (II)
Saugata Ghose, Amirali Boroumand, Jeremie S. Kim, Juan Gomez-Luna, and Onur Mutlu, "Processing-in-Memory: A Workload-Driven Perspective" Invited Article in IBM Journal of Research & Development, Special Issue on Hardware for Artificial Intelligence, to appear in November 2019. [Preliminary arXiv version]
https://arxiv.org/pdf/1907.12947.pdf

## Slide 117: More on Memory-Centric System Design
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures

## Slide 118: A Tutorial on PIM
Onur Mutlu, "Memory-Centric Computing Systems" Invited Tutorial at 66th International Electron Devices Meeting (IEDM), Virtual, 12 December 2020. [Slides (pptx) (pdf)] [Executive Summary Slides (pptx) (pdf)] [Tutorial Video (1 hour 51 minutes)] [Executive Summary Video (2 minutes)] [Abstract and Bio] [Related Keynote Paper from VLSI-DAT 2020] [Related Review Paper on Processing in Memory]
https://www.youtube.com/watch?v=H3sEaINPBOE
https://www.youtube.com/onurmutlulectures
https://www.youtube.com/watch?v=H3sEaINPBOE

## Slide 119: Special Research Sessions & Courses
Special Session at ISVLSI 2022: 9 cutting-edge talks
https://www.youtube.com/watch?v=qeukNs5XI3g

## Slide 120: Overview Readings (II)
Gagandeep Singh, Mohammed Alser, Damla Senol Cali, Dionysios Diamantopoulos, Juan Gomez-Luna, Henk Corporaal, Onur Mutlu,
“FPGA-Based Near-Memory Acceleration of Modern Data-Intensive Applications“
IEEE Micro, 2021.
[Source Code]
https://arxiv.org/pdf/2106.06433.pdf

## Slide 121: Overview Readings (III)
Mohammed Alser, Joel Lindegger, Can Firtina, Nour Almadhoun, Haiyu Mao, Gagandeep Singh, Juan Gomez-Luna, Onur Mutlu
“From Molecules to Genomic Variations: Intelligent Algorithms and Architectures for Intelligent Genome Analysis”
Computational and Structural Biotechnology Journal, 2022
[Source code]
https://arxiv.org/pdf/2205.07957.pdf

## Slide 122: Detailed Lectures on Genome Analysis
Computer Architecture, Fall 2020, Lecture 3a
  Introduction to Genome Sequence Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=CrRb32v7SJc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=5
Computer Architecture, Fall 2020, Lecture 8
  Intelligent Genome Analysis (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=ygmQpdDTL7o&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=14
Computer Architecture, Fall 2020, Lecture 9a
  GenASM: Approx. String Matching Accelerator (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=XoLpzmN-Pas&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=15
Accelerating Genomics Project Course, Fall 2020, Lecture 1
  Accelerating Genomics (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=rgjl8ZyLsAg&list=PL5Q2soXY2Zi9E2bBVAgCqLgwiDRQDTyId
https://www.youtube.com/onurmutlulectures

## Slide 123: Genomics (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=bioinformatics
Youtube Livestream:
  https://www.youtube.com/watch?v=DEL_5A_Y3TI&list=PL5Q2soXY2Zi8NrPDgOR1yRU_Cxxjw-u18
Project course
  Taken by Bachelor’s/Master’s students
  Genomics lectures
  Hands-on research exploration
  Many research readings

## Slide 124: Genomics (Fall 2021)
Fall 2021 Edition:
  https://safari.ethz.ch/projects_and_seminars/fall2021/doku.php?id=bioinformatics
Youtube Livestream:
  https://www.youtube.com/watch?v=MnogTeMjY8k&list=PL5Q2soXY2Zi8sngH-TrNZnDhDkPq55J9J
Project course
  Taken by Bachelor’s/Master’s students
  Genomics lectures
  Hands-on research exploration
  Many research readings

## Slide 125: Comp Arch (Fall’21)
Fall 2021 Edition:
  https://safari.ethz.ch/architecture/fall2021/doku.php?id=schedule
Fall 2020 Edition:
  https://safari.ethz.ch/architecture/fall2020/doku.php?id=schedule
Youtube Livestream (2021):
  https://www.youtube.com/watch?v=4yfkM_5EFgo&list=PL5Q2soXY2Zi-Mnk1PxjEIG32HAGILkTOF
Youtube Livestream (2020):
  https://www.youtube.com/watch?v=c3mPdZA-Fmc&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN
Master’s level course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  5 Simulator-based Lab Assignments
  Potential research exploration
  Many research readings
https://www.youtube.com/onurmutlulectures

## Slide 126: DDCA (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2022/doku.php?id=schedule
Spring 2021 Edition:
  https://safari.ethz.ch/digitaltechnik/spring2021/doku.php?id=schedule
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=cpXdE3HwvK0&list=PL5Q2soXY2Zi97Ya5DEUpMpO2bbAoaG7c6
Youtube Livestream (Spring 2021):
  https://www.youtube.com/watch?v=LbC0EZY8yw4&list=PL5Q2soXY2Zi_uej3aY39YB5pfW4SJ7LlN
Bachelor’s course
  2nd semester at ETH Zurich
  Rigorous introduction into “How Computers Work”
  Digital Design/Logic
  Computer Architecture
  10 FPGA Lab Assignments
https://www.youtube.com/onurmutlulectures

## Slide 127: Seminar in Comp Arch (Spring & Fall)
Spring 2022 Edition:
  https://safari.ethz.ch/architecture_seminar/spring2022/doku.php?id=schedule
Fall 2021 Edition:
  https://safari.ethz.ch/architecture_seminar/fall2021/doku.php?id=schedule
Youtube Livestream (Spring 2022):
  https://www.youtube.com/watch?v=rS9UPk509AQ&list=PL5Q2soXY2Zi_hxizriwKmFHgcoe2Q8-m0
Youtube Livestream (Fall 2021):
  https://www.youtube.com/watch?v=4TcP297mdsI&list=PL5Q2soXY2Zi_7UBNmC9B8Yr5JSwTG9yH4
Critical analysis course
  Taken by Bachelor’s/Masters/PhD students
  Cutting-edge research topics + fundamentals in Computer Architecture
  20+ research papers, presentations, analyses

## Slide 128: PIM Course (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=processing_in_memory
Youtube Livestream:
  https://www.youtube.com/watch?v=9e4Chnwdovo&list=PL5Q2soXY2Zi-841fUYYUK9EsXKhQKRPyX
Project course
  Taken by Bachelor’s/Master’s students
  Processing-in-Memory lectures
  Hands-on research exploration
  Many research readings

## Slide 129: Hetero. Systems (Spring’22)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=heterogeneous_systems
Youtube Livestream:
  https://www.youtube.com/watch?v=oFO5fTrgFIY&list=PL5Q2soXY2Zi9XrgXR38IM_FTjmY6h7Gzm
Project course
  Taken by Bachelor’s/Master’s students
  GPU and Parallelism lectures
  Hands-on research exploration
  Many research readings

## Slide 130: HW/SW Co-Design (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=hw_sw_codesign
Youtube Livestream:
  https://youtube.com/playlist?list=PL5Q2soXY2Zi8nH7un3ghD2nutKWWDk-NK
Project course
  Taken by Bachelor’s/Master’s students
  HW/SW co-design lectures
  Hands-on research exploration
  Many research readings

## Slide 131: SSD Course (Spring 2022)
Spring 2022 Edition:
  https://safari.ethz.ch/projects_and_seminars/spring2022/doku.php?id=modern_ssds
Youtube Livestream:
  https://www.youtube.com/watch?v=_q4rm71DsY4&list=PL5Q2soXY2Zi8vabcse1kL22DEcgMl2RAq
Project course
  Taken by Bachelor’s/Master’s students
  SSD Basics and Advanced Topics
  Hands-on research exploration
  Many research readings

## Slide 132: Funding Acknowledgments
Alibaba, AMD, ASML, Google, Facebook, Hi-Silicon, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware, Xilinx
NSF
NIH
GSRC
SRC
CyLab
EFCL

## Slide 133: Acknowledgments
Think BIG, Aim HIGH!
https://safari.ethz.ch

## Slide 134
40+ Researchers
Think BIG, Aim HIGH!
https://safari.ethz.ch
Onur Mutlu’s SAFARI Research Group
Computer architecture, HW/SW, systems, bioinformatics, security, memory
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 135: SAFARI Newsletter April 2020 Edition
https://safari.ethz.ch/safari-newsletter-april-2020/

## Slide 136: SAFARI Newsletter January 2021 Edition
https://safari.ethz.ch/safari-newsletter-january-2021/

## Slide 137: SAFARI Newsletter December 2021 Edition
https://safari.ethz.ch/safari-newsletter-december-2021/

## Slide 138: Referenced Papers, Talks, Artifacts
All are available at
  https://people.inf.ethz.ch/omutlu/projects.htm
  https://www.youtube.com/onurmutlulectures
  https://github.com/CMU-SAFARI/

## Slide 139: Open Source Tools: SAFARI GitHub
https://github.com/CMU-SAFARI/

## Slide 140: Some Recent Papers

## Slide 141: Connecting Basecalling and Read Mapping in PIM
Haiyu Mao, Mohammed Alser, Mohammad Sadrosadati, Can Firtina, Akanksha Baranwal, Damla Senol Cali, Aditya Manglik, Nour Almadhoun Alserr, and Onur Mutlu, ”GenPIP: In-Memory Acceleration of Genome Analysis via Tight Integration of Basecalling and Read Mapping" Proceedings of the 55th International Symposium on Microarchitecture (MICRO), Chicago, Illinois, October 2022.
Coming up at MICRO 2022

## Slide 142: Finding Approximate Seed Matches
Can Firtina, Jisung Park, Mohammed Alser, Jeremie S. Kim, Damla Senol Cali, Taha Shahroodi, Nika Mansouri-Ghiasi, Gagandeep Singh, Konstantinos Kanellopoulos, Can Alkan, and Onur Mutlu, "BLEND: A Fast, Memory-Efficient, and Accurate Mechanism to Find Fuzzy Seed Matches" Preprint in arXiv, 2021. [arXiv preprint] [BLEND Source Code and Data]

## Slide 143: Hardware Acceleration for pHMMs
Can Firtina, Kamlesh Pillai, Gurpreet S. Kalsi, Bharathwaj Suresh, Damla Senol Cali, Jeremie S. Kim, Taha Shahroodi, Meryem Banu Cavlak, Joel Lindegger, Mohammed Alser, Juan Gómez-Luna, Sreenivas Subramoney, and Onur Mutlu, "ApHMM: A Profile Hidden Markov Model Acceleration Framework for Genome Analysis" Preprint in arXiv, 2022. [Source Code]

## Slide 144: Remapping Reads Between References
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Nastaran Hajinazar, Mohammed Alser, Can Alkan, and Onur Mutlu, "AirLift: A Fast and Comprehensive Technique for Remapping Alignments between Reference Genomes" Preprint in arXiv and bioRxiv, 2021. [bioRxiv preprint] [arXiv preprint] [AirLift Source Code and Data]

## Slide 145: Mapping Constant Regions Between References
Jeremie S. Kim, Can Firtina, Meryem Banu Cavlak, Damla Senol Cali, Can Alkan, and Onur Mutlu, "FastRemap: A Tool for Quickly Remapping Reads between Genome Assemblies" Bioinformatics, btac554. [FastRemap Source Code]

## Slide 146: COVIDHunter
Mohammed Alser, Jeremie S. Kim, Nour Almadhoun Alserr, Stefan W. Tell,
Onur Mutlu
“COVIDHunter: COVID-19 Pandemic Wave Prediction and Mitigation via Seasonality Aware Modeling”
Frontiers in Public Health 2022
[Source Code]

## Slide 147: Packaging Omics Methods
Mohammed Alser, Sharon Waymost, Ram Ayyala, Brendan Lawlor, Richard J. Abdill, Neha Rajkumar, Nathan LaPierre, Jaqueline Brito, Andre M. Ribeiro-dos-Santos, Can Firtina, Nour Almadhoun, Varuni Sarwal, Eleazar Eskin, Qiyang Hu, Derek Strong, Byoung-Do (BD)Kim, Malak S. Abedalthagafi, Onur Mutlu, Serghei Mangul
“Packaging, containerization, and virtualization of computational omics methods: Advances, challenges, and opportunities”
arrXiv 2022

## Slide 148: Demeter (HD Food Microbiome Profiling)
Taha Shahroodi, Mahdi Zahedi, Can Firtina, Mohammed Alser, Stephan Wong,
Onur Mutlu, Said Hamdioui
“Demeter: A Fast and Energy-Efficient Food Profiler using Hyperdimensional Computing in Memory”
IEEE Access, 2022

## Slide 149: AIM (PIM Sequence Alignment Framework)
Safaa Diab, Amir Nassereldine, Mohammed Alser, Juan Gómez-Luna,
Onur Mutlu, Izzat El Hajj
“A Framework for High-throughput Sequence Alignment using Real Processing-in-Memory Systems“
arXiv, 2022
[Source code]

## Slide 150: Scrooge
Joël Lindegger, Damla Senol Cali, Mohammed Alser, Juan Gómez-Luna,
Nika Mansouri Ghiasi, Onur Mutlu
“Scrooge: A Fast and Memory-Frugal Genomic Sequence Aligner for CPUs, GPUs, and ASICs“
arXiv, 2022
[Source code]

## Slide 151: Intelligent Genome Analysis
Mohammed Alser, Joel Lindegger, Can Firtina, Nour Almadhoun, Haiyu Mao, Gagandeep Singh, Juan Gomez-Luna, Onur Mutlu
“From Molecules to Genomic Variations: Intelligent Algorithms and Architectures for Intelligent Genome Analysis”
Computational and Structural Biotechnology Journal, 2022
[Source code]

## Slide 152: Pairwise Sequence Alignment using PIM
Safaa Diab, Amir Nassereldine, Mohammed Alser, Juan Gómez Luna, Onur Mutlu, and Izzat El Hajj, "High-throughput Pairwise Alignment with the Wavefront Algorithm using Processing-in-Memory" Preprint in arXiv, 2022.

## Slide 153: Detailed Lectures on PIM (I)
Computer Architecture, Fall 2020, Lecture 6
  Computation in Memory (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=oGcZAGwfEUE&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=12
Computer Architecture, Fall 2020, Lecture 7
  Near-Data Processing (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=j2GIigqn1Qw&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=13
Computer Architecture, Fall 2020, Lecture 11a
  Memory Controllers (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=TeG773OgiMQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=20
Computer Architecture, Fall 2020, Lecture 12d
  Real Processing-in-DRAM with UPMEM (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=Sscy1Wrr22A&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=25
https://www.youtube.com/onurmutlulectures

## Slide 154: Detailed Lectures on PIM (II)
Computer Architecture, Fall 2020, Lecture 15
  Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=AlE1rD9G_YU&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=28
Computer Architecture, Fall 2020, Lecture 16a
  Opportunities & Challenges of Emerging Memory Technologies (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=pmLszWGmMGQ&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=29
Computer Architecture, Fall 2020, Guest Lecture
  In-Memory Computing: Memory Devices & Applications (ETH Zürich, Fall 2020)
  https://www.youtube.com/watch?v=wNmqQHiEZNk&list=PL5Q2soXY2Zi9xidyIgBxUz7xRPS-wisBN&index=41
https://www.youtube.com/onurmutlulectures

## Slide 155: End of Backup Slides