## Slide 1: Rethinking Memory System Design (for Data-Intensive Computing)
Onur Mutlu
onur@cmu.edu
http://users.ece.cmu.edu/~omutlu/
July 20, 2015
SAMOS Keynote

## Slide 2: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processor
and caches
Main Memory
Storage (SSD/HDD)

## Slide 3: Memory System: A Shared Resource View
Storage

## Slide 4: State of the Main Memory System
Recent technology, architecture, and application trends
  lead to new requirements
  exacerbate old requirements
DRAM and memory controllers, as we know them today, are (will be) unlikely to satisfy all requirements
Some emerging non-volatile memory technologies (e.g., PCM) enable new opportunities: memory+storage merging
We need to rethink the main memory system
  to fix DRAM issues and enable emerging technologies
  to satisfy all requirements

## Slide 5: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
How Can We Do Better?
Summary

## Slide 6: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 7: Major Trends Affecting Main Memory (II)
Need for main memory capacity, bandwidth, QoS increasing
  Multi-core: increasing number of cores/agents
  Data-intensive applications: increasing demand/hunger for data
  Consolidation: cloud computing, GPUs, mobile, heterogeneity
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 8: Example: The Memory Capacity Gap
Memory capacity per core expected to drop by 30% every two years
Trends worse for memory bandwidth per core!
Core count doubling ~ every 2 years
DRAM DIMM capacity doubling ~ every 3 years

## Slide 9: Major Trends Affecting Main Memory (III)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
  ~40-50% energy spent in off-chip memory hierarchy [Lefurgy, IEEE Computer 2003]
  DRAM consumes power even when not used (periodic refresh)
DRAM technology scaling is ending

## Slide 10: Major Trends Affecting Main Memory (IV)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending
  ITRS projects DRAM will not scale easily below X nm
  Scaling has provided many benefits:
    higher capacity (density), lower cost, lower energy

## Slide 11: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
How Can We Do Better?
Summary

## Slide 12: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 13: An Example of The Scaling Problem
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Hammered Row
Repeatedly opening and closing a row induces disturbance errors in adjacent rows in most real DRAM chips [Kim+ ISCA 2014]
Opened
Closed

## Slide 14: Most DRAM Modules Are At Risk
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.

## Slide 15
DRAM Module
x86 CPU
Y
X
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
  https://github.com/CMU-SAFARI/rowhammer
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 16
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  https://github.com/CMU-SAFARI/rowhammer
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 17
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  https://github.com/CMU-SAFARI/rowhammer
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 18
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
  https://github.com/CMU-SAFARI/rowhammer
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 19: Observed Errors in Real Systems
A real reliability & security issue
In a more controlled environment, we can induce as many as ten million disturbance errors
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: When we executed the code on four different processors, all four of them yielded errors. Intel Haswell has the most errors, at 23 thousand, because it has the highest rate of accessing DRAM.
Later on, I’ll show that we can induce as many as ten million disturbance errors in a more controlled environment.
From this, we conclude that disturbance errors are a serious reliability issue.

## Slide 20: Errors vs. Vintage
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 21: Experimental Infrastructure (DRAM)
  Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms”, ISCA 2013.
  Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors”, ISCA 2014.
  Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.
  Qureshi+, “AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems,” DSN 2015.

## Slide 22: Experimental Infrastructure (DRAM)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 23: RowHammer Characterization Results
Most Modules Are at Risk
Errors vs. Vintage
Error = Charge Loss
Adjacency: Aggressor & Victim
Sensitivity Studies
Other Results in Paper
Solution Space
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: Now I will present the characterization results, one-by-one.
First, I show that most modules are at risk. Second, I show the number of errors in a module as a function of the manufacture date. Third, I show that the errors are symptomatic of charge loss. Fourth, I show that an aggressor induces errors in adjacent rows. Fifth, I show several sensitivity studies. And, finally, I briefly describe other results in the paper.

## Slide 24: Security Implications
http://googleprojectzero.blogspot.com/2015/03/exploiting-dram-rowhammer-bug-to-gain.html
http://users.ece.cmu.edu/~omutlu/pub/dram-row-hammer_isca14.pdf

## Slide 25: Security Implications
Notes: Picture from the article:
http://thehackernews.com/2015/03/dram-rowhammer-vulnerability.html

## Slide 26: Recap: The DRAM Scaling Problem

## Slide 27: How Do We Solve The Problem?
Fix it: Make DRAM and controllers more intelligent
  New interfaces, functions, architectures: system-DRAM codesign
Eliminate or minimize it: Replace or (more likely) augment DRAM with a different technology
  New technologies and system-wide rethinking of memory & storage
Embrace it: Design heterogeneous memories (none of which are perfect) and map data intelligently across them
  New models for data management and maybe usage
…
Solutions (to memory scaling) require
software/hardware/device cooperation
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 28: Solution 1: Fix DRAM
Overcome DRAM shortcomings with
  System-DRAM co-design
  Novel DRAM architectures, interface, functions
  Better waste management (efficient utilization)
Key issues to tackle
  Enable reliability at low cost
  Reduce energy
  Improve latency and bandwidth
  Reduce waste (capacity, bandwidth, latency)
  Enable computation close to data

## Slide 29: Solution 1: Fix DRAM
Liu+, “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.
Kim+, “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices,” ISCA 2013.
Seshadri+, “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.
Pekhimenko+, “Linearly Compressed Pages: A Main Memory Compression Framework,” MICRO 2013.
Chang+, “Improving DRAM Performance by Parallelizing Refreshes with Accesses,” HPCA 2014.
Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Luo+, “Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost,” DSN 2014.
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.
Qureshi+, “AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems,” DSN 2015.
Meza+, “Revisiting Memory Errors in Large-Scale Production Data Centers: Analysis and Modeling of New Trends from the Field,” DSN 2015.
Kim+, “Ramulator: A Fast and Extensible DRAM Simulator,” IEEE CAL 2015.
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM,” IEEE CAL 2015.
Ahn+, “A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing,” ISCA 2015.
Ahn+ “PIM-Enabled Instructions: A Low-Overhead, Locality-Aware Processing-in-Memory Architecture,” ISCA 2015.
Avoid DRAM:
  Seshadri+, “The Evicted-Address Filter: A Unified Mechanism to Address Both Cache Pollution and Thrashing,” PACT 2012.
  Pekhimenko+, “Base-Delta-Immediate Compression: Practical Data Compression for On-Chip Caches,” PACT 2012.
  Seshadri+, “The Dirty-Block Index,” ISCA 2014.
  Pekhimenko+, “Exploiting Compressed Block Size as an Indicator of Future Reuse,” HPCA 2015.
  Vijaykumar+, “A Case for Core-Assisted Bottleneck Acceleration in GPUs: Enabling Flexible Data Compression with Assist Warps,” ISCA 2015.

## Slide 30: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Expected to scale to 9nm (2022 [ITRS])
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have shortcomings as well
  Can they be enabled to replace/augment/surpass DRAM?
Lee+, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA’09, CACM’10, Micro’10.
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters 2012.
Yoon, Meza+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012.
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Lu+, “Loose Ordering Consistency for Persistent Memory,” ICCD 2014.
Zhao+, “FIRM: Fair and High-Performance Memory Control for Persistent Memory Systems,” MICRO 2014.
Yoon, Meza+, “Efficient Data Mapping and Buffering Techniques for Multi-Level Cell Phase-Change Memories,” ACM TACO 2014.
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 31: Solution 3: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon, Meza et al., “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Technology X (e.g., PCM)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 32: Exploiting Memory Error Tolerance with Hybrid Memory Systems
Chart: Memory error vulnerability
| App/Data A | App/Data B | App/Data C
System/Application Crash | 1.0414 | 0.63898 | 0.24773
Vulnerable data
Tolerant data
Heterogeneous-Reliability Memory [DSN 2014]
Low-cost memory
Reliable memory
Vulnerable data
Tolerant data
Vulnerable data
Tolerant data
ECC protected
Well-tested chips
NoECC or Parity
Less-tested chips
  On Microsoft’s Web Search workload
  Reduces server hardware cost by 4.7 %
  Achieves single server availability target of 99.90 %
Notes: As we have shown earlier, either across or within applications, our characterization can identify data that are vulnerable to memory errors and data that are tolerant to memory errors.
To exploit this observation, we would like to map these different data onto different memory modules according to their memory error tolerance.
As an example here, we map vulnerable data to reliable memory to improve reliability, and map tolerant data to low-cost less-reliable memory to exploit its tolerance and lower the cost. We call this mechanism heterogeneous-reliability memory, HRM.
Reliable memory consists of … Low cost memory consists of …
As we will show later, HRM allows us to use weaker error protection in memory, and enables the use of less-tested memory chips to lower the cost of the memory system, while still achieving reasonable single-server reliability target.

## Slide 33: An Orthogonal Issue: Memory Interference
Main
Memory
Core
Core
Core
Core
Cores’ interfere with each other when accessing shared main memory
Notes: In a multicore system, multiple applications running on the different cores share the main memory.
These applications interfere at the main memory. The result of this interference is unpredictable application slowdowns.

## Slide 34: An Orthogonal Issue: Memory Interference
Problem: Memory interference between cores is uncontrolled
   unfairness, starvation, low performance
   uncontrollable, unpredictable, vulnerable system
Solution: QoS-Aware Memory Systems
  Hardware designed to provide a configurable fairness substrate
    Application-aware memory scheduling, partitioning, throttling
  Software designed to configure the resources to satisfy different QoS goals
QoS-aware memory systems can provide predictable performance and higher efficiency

## Slide 35: Goal: Predictable Performance in Complex Systems
Heterogeneous agents: CPUs, GPUs, and HWAs
Main memory interference between CPUs, GPUs, HWAs
CPU
CPU
CPU
CPU
Shared Cache
GPU
HWA
HWA
DRAM and Hybrid Memory Controllers
DRAM and Hybrid Memories
How to allocate resources to heterogeneous agents
to mitigate interference and provide predictable performance?

## Slide 36: Strong Memory Service Guarantees
Goal: Satisfy performance/SLA requirements in the presence of shared main memory, heterogeneous agents, and hybrid memory/storage
Approach:
  Develop techniques/models to accurately estimate the performance loss of an application/agent in the presence of resource sharing
  Develop mechanisms (hardware and software) to enable the resource partitioning/prioritization needed to achieve the required performance levels for all applications
  All the while providing high system performance
Example work: Subramanian et al., “MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems,” HPCA 2013.

## Slide 37: Some Promising Directions
New memory architectures
  Rethinking DRAM and flash memory
  A lot of hope in fixing DRAM
Enabling emerging NVM technologies
  Hybrid memory systems
  Single-level memory and storage
  A lot of hope in hybrid memory systems and single-level stores
System-level memory/storage QoS
  A lot of hope in designing a predictable system

## Slide 38: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
How Can We Do Better?
Summary

## Slide 39: Rethinking DRAM
In-Memory Computation
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 40: Today’s Memory: Bulk Data Copy
Memory
MC
L3
L2
L1
CPU
1) High latency
2) High bandwidth utilization
3) Cache pollution
4) Unwanted data movement
1046ns, 3.6uJ (for 4KB page copy via DMA)

## Slide 41: Future: RowClone (In-Memory Copy)
Memory
MC
L3
L2
L1
CPU
1) Low latency
2) Low bandwidth utilization
3) No cache pollution
4) No unwanted data movement
1046ns, 3.6uJ
90ns, 0.04uJ

## Slide 42: DRAM Subarray Operation (load one byte)
Row Buffer (8 Kbits)
Data Bus
8 bits
DRAM array
8 Kbits
Step 1: Activate row
Transfer row
Step 2: Read
Transfer byte onto bus
Notes: say you want a byte

## Slide 43: RowClone: In-DRAM Row Copy
Row Buffer (8 Kbits)
Data Bus
8 bits
DRAM array
8 Kbits
Step 1: Activate row A
Transfer row
Step 2: Activate row B
Transfer
row
0.01% area cost
Notes: copy

## Slide 44: Generalized RowClone
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Intra Subarray
Copy (2 ACTs)
Inter Bank Copy
(Pipelined
Internal RD/WR)
Inter Subarray Copy
(Use Inter-Bank Copy Twice)

## Slide 45: RowClone: Latency and Energy Savings
Chart: Normalized Savings
| Latency | Energy
Baseline | 1 | 1
Intra-Subarray | 0.088583 | 0.013449
Inter-Bank | 0.51673 | 0.31183
Inter-Subarray | 1.0148 | 0.6785
11.6x
74x
Seshadri et al., “RowClone: Fast and Efficient In-DRAM Copy and Initialization of Bulk Data,” MICRO 2013.

## Slide 46: RowClone: Application Performance
Chart: % Compared to Baseline
| bootup | compile | forkbench | mcached | mysql | shell
IPC Improvement | 15 | 9 | 43 | 4 | 4 | 40
Energy Reduction | 40 | 32 | 60 | 15 | 17 | 67

## Slide 47: RowClone: Multi-Core Performance
Chart: 50 Workloads (4-core)
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
RowClone | 1.02 | 1.04 | 1.07 | 1.07 | 1.08 | 1.08 | 1.08 | 1.08 | 1.08 | 1.09 | 1.09 | 1.09 | 1.1 | 1.1 | 1.11 | 1.11 | 1.12 | 1.12 | 1.12 | 1.12 | 1.13 | 1.15 | 1.16 | 1.16 | 1.18 | 1.2 | 1.2 | 1.2 | 1.2 | 1.21 | 1.21 | 1.21 | 1.21 | 1.23 | 1.23 | 1.23 | 1.23 | 1.24 | 1.26 | 1.27 | 1.27 | 1.27 | 1.28 | 1.3 | 1.31 | 1.32 | 1.32 | 1.34 | 1.34 | 1.39

## Slide 48: End-to-End System Design
DRAM (RowClone)
Microarchitecture
ISA
Operating System
Application
How to communicate occurrences of bulk copy/initialization across layers?
How to maximize latency and energy savings?
How to ensure cache coherence?
How to handle data reuse?

## Slide 49: Goal: Ultra-Efficient Processing Near Data
CPU
core
CPU
core
CPU
core
CPU
core
mini-CPU
core
video
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
GPU
(throughput)
core
LLC
Memory Controller
Specialized
compute-capability
in memory
Memory
imaging
core
Memory Bus
Memory similar to a “conventional” accelerator

## Slide 50: Enabling In-Memory Search
What is a flexible and scalable memory interface?
What is the right partitioning of computation capability?
What is the right low-cost memory substrate?
What memory technologies are the best enablers?
How do we rethink/ease search algorithms/applications?
Cache
Processor
Core
Interconnect
Memory
Database
Query vector
Results

## Slide 51: Enabling In-Memory Computation
Virtual Memory Support
Cache Coherence
DRAM Support
RowClone
(MICRO 2013)
Dirty-Block Index
(ISCA 2014)
Page Overlays
(ISCA 2015)
In-DRAM Gather Scatter
In-DRAM Bitwise Operations
(IEEE CAL 2015)
?
?
Non-contiguous Cache lines
Gathered Pages

## Slide 52: In-DRAM AND/OR: Triple Row Activation
½VDD
½VDD
dis
A
B
C
Final State
AB + BC + AC
½VDD+δ
C(A + B) + ~C(AB)
en
0
VDD
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.

## Slide 53: In-DRAM AND/OR Results
20X improvement in AND/OR throughput vs. Intel AVX
50.5X reduction in memory energy consumption
At least 30% performance improvement in range queries
Seshadri+, “Fast Bulk Bitwise AND and OR in DRAM”, IEEE CAL 2015.
Size of Vectors to be ANDed
Throughput of AND operations (GB/s)
In-DRAM AND (2 banks)
In-DRAM AND (1 bank)
Intel AVX

## Slide 54: Rethinking DRAM
In-Memory Computation
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 55: DRAM Refresh
DRAM capacitor charge leaks over time
The memory controller needs to refresh each row periodically to restore charge
  Activate each row every N ms
  Typical N = 64 ms
Downsides of refresh
-- Energy consumption: Each refresh consumes energy
  -- Performance degradation: DRAM rank/bank unavailable while refreshed
  -- QoS/predictability impact: (Long) pause times during refresh
  -- Refresh rate limits DRAM capacity scaling

## Slide 56: Refresh Overhead: Performance
8%
46%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 57: Refresh Overhead: Energy
15%
47%
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 58: Retention Time Profile of DRAM

## Slide 59: RAIDR: Eliminating Unnecessary Refreshes
Observation: Most DRAM rows can be refreshed much less often without losing data [Kim+, EDL’09][Liu+ ISCA’13]
Key idea: Refresh rows containing weak cells
more frequently, other rows less frequently
  1. Profiling: Profile retention time of all rows
  2. Binning: Store rows into bins by retention time in memory controller
  Efficient storage with Bloom Filters (only 1.25KB for 32GB memory)
  3. Refreshing: Memory controller refreshes rows in different bins at different rates
Results: 8-core, 32GB, SPEC, TPC-C, TPC-H
  74.6% refresh reduction @ 1.25KB storage
  ~16%/20% DRAM dynamic/idle power reduction
  ~9% performance improvement
  Benefits increase with DRAM capacity
Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012.

## Slide 60: Going Forward (for DRAM and Flash)
How to find out weak memory cells/rows
  Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms”, ISCA 2013.
  Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
Low-cost system-level tolerance of memory errors
  Luo+, “Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost,” DSN 2014.
  Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
  Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Tolerating cell-to-cell interference at the system level
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
  Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.

## Slide 61: Experimental Infrastructure (DRAM)
  Liu+, “An Experimental Study of Data Retention Behavior in Modern DRAM Devices: Implications for Retention Time Profiling Mechanisms”, ISCA 2013.
  Khan+, “The Efficacy of Error Mitigation Techniques for DRAM Retention Failures: A Comparative Experimental Study,” SIGMETRICS 2014.
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors”, ISCA 2014.
  Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.
  Qureshi+, “AVATAR: A Variable-Retention-Time (VRT) Aware Refresh for DRAM Systems,” DSN 2015.

## Slide 62: Experimental Infrastructure (DRAM)
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 63: More Information [ISCA’13, SIGMETRICS’14]

## Slide 64: Online Profiling of DRAM In the Field
Optimize DRAM and mitigate errors online
without disturbing the system and applications
Initially protect DRAM
with ECC
1
Periodically test
parts of DRAM
2
ECC
Test
Test
Test
Adjust refresh rate and
reduce ECC
3
Notes: Based on these observations, we propose that in an online profiling system,

## Slide 65: Rethinking DRAM
In-Memory Computation
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 66
DRAM Latency-Capacity Trend
Chart: Year
| 2000.0 | 2003.0 | 2006.0 | 2008.0 | 2011.0
Capacity | 0.125 | 0.25 | 0.5 | 1 | 2
Latency (tRC) | 65 | 60 | 57.5 | 49.5 | 47.91
16X
-20%
DRAM latency continues to be a critical bottleneck, especially for response time-sensitive workloads
Notes: The figure shows the historical trends of DRAM during the last 12-years, from 2000 to 2011.
We can see that, during this time, DRAM capacity has increased by 16 times.
On the other hand, during the same period of time, DRAM latency has reduced by only 20%.
As a result, the high DRAM latency continues to be a critical bottleneck for system performance.

## Slide 67: What Causes the Long Latency?
DRAM Latency = Subarray Latency + I/O Latency
DRAM Chip
channel
cell array
I/O
DRAM Chip
channel
I/O
subarray
DRAM Latency = Subarray Latency + I/O Latency
Dominant
Subarray
I/O
Notes: To understand what causes the long latency, let me take a look at the DRAM organization.
DRAM consists of two components, the cell array and the I/O circuitry. The cell array consists of multiple subarrays.
To read from a DRAM chip, the data is first accessed from the subarray and then the data is transferred over the channel by the I/O circuitry.
So, the DRAM latency is the sum of the subarray latency and the I/O latency.
We observed that the subarray latency is much higher than the I/O latency.
As a result, subarray is the dominant source of the DRAM latency as we explained in the paper.

## Slide 68: Why is the Subarray So Slow?
Subarray
row decoder
sense amplifier
capacitor
access
transistor
wordline
bitline
Cell
large sense amplifier
bitline: 512 cells
cell
Long bitline
  Amortizes sense amplifier cost  Small area
  Large bitline capacitance  High latency & power
sense amplifier
row decoder
Notes: The cell’s capacitor is small and can store only a small amount of charge.
That is why a subarray also has sense-amplifiers, which are specialized circuits that can detect the small amount of charge.
Unfortunately, a sense-amplifier size is about *100* times the cell size.
So, to amortize the area of the sense-amplifiers,
hundreds of cells share the same sense-amplifier through a long bitline.
However, a long bitline has a large capacitance that increases latency and power consumption.
Therefore, the long bitline is one of the dominant sources of high latency and high power consumption.
To understand why the subarray is so slow,
let me take a look at the subarray organization.

## Slide 69: Trade-Off: Area (Die Size) vs. Latency
Faster
Smaller
Short Bitline
Long Bitline
Trade-Off: Area vs. Latency
Notes: A naïve way to reduce the DRAM latency is to have short bitlines that have lower latency.
Unfortunately, short bitlines significantly increase the DRAM area.
Therefore, the bitline length exposes an important trade-off between area and latency.

## Slide 70: Trade-Off: Area (Die Size) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.61776435004466 | 27.83117556055124 | 35.46159936378587 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Commodity DRAM
Long Bitline
Cheaper
Faster
Fancy DRAM
Short Bitline
GOAL
Notes: This figure shows the trade-off between DRAM area and latency as we change the bitline length.
Y-axis is the normalized DRAM area compared to a DRAM using 512 cells/bitline. A lower value is cheaper.
X-axis shows the latency in terms of tRC, an important DRAM timing constraint. A lower value is faster.
Commodity DRAM chips use long bitlines to minimize area cost. On the other hand, shorter bitlines achieve lower latency at higher cost.
Our goal is to achieve the best of both worlds: low latency and low area cost.

## Slide 71: Approximating the Best of Both Worlds
Short Bitline
Low Latency
Long Bitline
Small Area
Long Bitline
Low Latency
Short Bitline
Our Proposal
Small Area
Short Bitline  Fast
Need Isolation
Add Isolation Transistors
High Latency
Large Area
Notes: To sum up, both long and short bitline do not achieve small area and low latency.
Long bitline has small area but has high latency while short bitline has low latency but has large area.
To achieve the best of both worlds, we first start from long bitline, which has small area.
After that, to achieve the low latency of short bitline, we divide the long bitline into two smaller segments.
The bitline length of the segment nearby the sense-amplifier is same as the length of short bitline.
Therefore, the latency of the segment is as low as the latency of the short bitline.
To isolate this fast segment from the other segment, we add isolation transistors that selectively connect the two segments.

## Slide 72: Approximating the Best of Both Worlds
Low Latency
Our Proposal
Small Area
Long Bitline
Small Area
Long Bitline
High Latency
Short Bitline
Low Latency
Short Bitline
Large Area
Tiered-Latency DRAM
Low Latency
Small area using long bitline
Notes: This way, our proposed approach achieves small area and low latency.
We call this new DRAM architecture as Tiered-Latency DRAM

## Slide 73: Commodity DRAM vs. TL-DRAM [HPCA 2013]
Chart: 
| commodity DRAM | near segment | far segment
Normalized Power Consumption | 1 | 0.49 | 1.49
Chart: 
| commodity DRAM | near segment | far segment
Latency | 1 | 0.56 | 1.23
Latency
Power
  –56%
  +23%
  –51%
  +49%
DRAM Latency (tRC)
DRAM Power
DRAM Area Overhead
  ~3%: mainly due to the isolation transistors
  TL-DRAM
  Commodity DRAM
  Near Far
  Commodity DRAM
  Near Far
  TL-DRAM
  (52.5ns)
Notes: This figure compares the latency.
Y-axis is normalized latency.
Compared to commodity DRAM, TL-DRAM’s near segment has 56% lower latency, while the far segment has 23% higher latency.
The right figure compares the power.
Y-axis is normalized power.
Compared to commodity DRAM, TL-DRAM’s near segment has 51% lower power consumption and the far segment has 49% higher power consumption.
Lastly, mainly due to the isolation transistor, Tiered-latency DRAM increases the die-size by about 3%.

## Slide 74: Trade-Off: Area (Die-Area) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.61776435004466 | 27.83117556055124 | 35.46159936378587 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Cheaper
Faster
Near Segment
Far Segment
GOAL
Notes: Again, the figure shows the trade-off between area and latency in existing DRAM.
Unlike existing DRAM, TL-DRAM achieves low latency using the near segment while increasing the area by only 3%.
Although the far segment has higher latency than commodity DRAM, we show that efficient use of the near segment enables TL-DRAM to achieve high system performance.

## Slide 75: Leveraging Tiered-Latency DRAM
TL-DRAM is a substrate that can be leveraged by the hardware and/or software
Many potential uses
  Use near segment as hardware-managed inclusive cache to far segment
  Use near segment as hardware-managed exclusive cache to far segment
  Profile-based page mapping by operating system
  Simply replace DRAM with TL-DRAM
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: There are multiple ways to leverage the TL-DRAM substrate by hardware or software.
In this slide, I describe many such ways.
First, the near segment can be used as a hardware-managed inclusive cache to the far segment.
Second, the near segment can be used as a hardware-managed exclusive cache to the far segment.
Third, the operating system can intelligently allocate frequently-accessed pages to the near segment.
Forth mechanism is to simple replace DRAM with TL-DRAM without any near segment handling
While our paper provides detailed explanations and evaluations of first three mechanism,
in this talk, we will focus on the first approach, which is to use the near segment as a hardware managed cache for the far segment.

## Slide 76: Performance & Power Consumption
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Performance Improvement | 1.124 | 1.115 | 1.107
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Power Reduction | 0.769 | 0.755 | 0.737
11.5%
Normalized Performance
Core-Count (Channel)
Normalized Power
Core-Count (Channel)
10.7%
12.4%
–23%
–24%
–26%
Using near segment as a cache improves performance and reduces power consumption
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: This figure shows the IPC improvement of our three caching mechanisms over commodity DRAM.
All of them improve performance and benefit-based caching shows maximum performance improvement by 12.7%.
The right figure shows the normalized power reduction of our three caching mechanisms over commodity DRAM.
All of them reduce power consumption and benefit-based caching shows maximum power reduction by 23%.
Therefore, using near segment as a cache improves performance and reduces power consumption at the cost of 3% area overhead.

## Slide 77: What Else Causes the Long DRAM Latency?
Conservative timing margins!
DRAM timing parameters are set to cover the worst case
Worst-case temperatures
  85 degrees vs. common-case
  to enable a wide range of operating conditions
Worst-case devices
  DRAM cell with smallest charge across any acceptable device
  to tolerate process variation at acceptable yield
This leads to large timing margins for the common case

## Slide 78: Adaptive-Latency DRAM [HPCA 2015]
Idea: Optimize DRAM timing for the common case
  Current temperature
  Current DRAM module
Why would this reduce latency?
  A DRAM cell can store much more charge in the common case (low temperature, strong cell) than in the worst case
  More charge in a DRAM cell
   Faster sensing, charge restoration, precharging
   Faster access (read, write, refresh, …)
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 79: AL-DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer provides multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 80
Latency Reduction Summary of 115 DIMMs
Latency reduction for read & write (55°C)
  Read Latency: 32.7%
  Write Latency: 55.1%
Latency reduction for each timing parameter (55°C)
  Sensing: 17.3%
  Restore: 37.3% (read), 54.8% (write)
  Precharge: 35.2%
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 81
AL-DRAM: Real System Evaluation
System
  CPU: AMD 4386 ( 8 Cores, 3.1GHz, 8MB LLC)
  DRAM: 4GByte DDR3-1600 (800Mhz Clock)
  OS: Linux
  Storage: 128GByte SSD
Workload
  35 applications from SPEC, STREAM, Parsec, Memcached, Apache, GUPS

## Slide 82
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
1.4%
6.7%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
5.0%
AL-DRAM: Single-Core Evaluation
AL-DRAM improves performance on a real system
Performance Improvement
Average
Improvement
all-35-workload

## Slide 83
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
AL-DRAM: Multi-Core Evaluation
AL-DRAM provides higher performance for
multi-programmed & multi-threaded workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 84: Rethinking DRAM
In-Memory Computation
Refresh
Reliability
Latency
Bandwidth
Energy
Memory Compression

## Slide 85: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
How Can We Do Better?
Summary

## Slide 86: Solution 2: Emerging Memory Technologies
Some emerging resistive memory technologies seem more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Data stored by changing phase of material
  Data read by detecting material’s resistance
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have (many) shortcomings
  Can they be enabled to replace/augment/surpass DRAM?
Notes: Even if DRAM continues to scale there could be benefits to examining and enabling these new technologies.

## Slide 87: Limits of Charge Memory
Difficult charge placement and control
  Flash: floating gate charge
  DRAM: capacitor charge, transistor leakage
Reliable sensing becomes difficult as charge storage unit size reduces

## Slide 88: Promising Resistive Memory Technologies
PCM
  Inject current to change material phase
  Resistance determined by phase
STT-MRAM
  Inject current to change magnet polarity
  Resistance determined by polarity
Memristors/RRAM/ReRAM
  Inject current to change atomic structure
  Resistance determined by atom distance

## Slide 89: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatility
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
  Reliability issues (resistance drift)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system

## Slide 90: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM

## Slide 91: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings

## Slide 92: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 93: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 94: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 95: Solution 3: Hybrid Memory Systems
Meza+, “Enabling Efficient and Scalable Hybrid Memories,” IEEE Comp. Arch. Letters, 2012.
Yoon+, “Row Buffer Locality Aware Caching Policies for Hybrid Memories,” ICCD 2012 Best Paper Award.
CPU
DRAMCtrl
Fast, durable
Small,
leaky, volatile,
high-cost
Large, non-volatile, low-cost
Slow, wears out, high active energy
PCM Ctrl
DRAM
Phase Change Memory (or Tech. X)
Hardware/software manage data allocation and movement
to achieve the best of multiple technologies

## Slide 96: Hybrid vs. All-PCM/DRAM [ICCD’12]
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
31% better performance than all PCM,
within 29% of all DRAM performance
31%
29%
Yoon+, “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 97: STT-MRAM as Main Memory
Magnetic Tunnel Junction (MTJ) device
  Reference layer: Fixed magnetic orientation
  Free layer: Parallel or anti-parallel
Magnetic orientation of the free layer determines logical state of device
  High vs. low resistance
Write: Push large current through MTJ to change orientation of free layer
Read: Sense current flow
Kultursay et al., “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.
Reference Layer
Free Layer
Barrier
Reference Layer
Free Layer
Barrier
Logical 0
Logical 1
Word Line
Bit Line
Access
Transistor
MTJ
Sense Line
Notes: Moving from DRAM to STT-RAM, instead of a capacitor that stores charge, now we have a magnetic tunnel junction that has one reference layer with a fixed magnetic orientation, and a free layer that can be parallel or anti parallel to the reference layer; which determines the resistance, and in turn, the data stored in the MTJ. In addition to the MTJ, the cell, again, has an access transistor.
Reading requires a small voltage to be applied across the bitline and sense line; and the current is sensed. This current varies depending on the resistance of MTJ. To write data, we push a large current into the MTJ, which re-aligns the free layer. The direction of the current determines whether it becomes parallel or anti-parallel; i.e. logical 0 or 1.

## Slide 98: STT-MRAM: Pros and Cons
Pros over DRAM
  Better technology scaling
  Non volatility
  Low idle power (no refresh)
Cons
  Higher write latency
  Higher write energy
  Reliability?
Another level of freedom
  Can trade off non-volatility for lower write latency/energy (by reducing the size of the MTJ)

## Slide 99: Architected STT-MRAM as Main Memory
4-core, 4GB main memory, multiprogrammed workloads
~6% performance loss, ~60% energy savings vs. DRAM
Chart: Performance vs. DRAM
STT-RAM (base) | 0.95574 | 0.91812 | 0.93435 | 0.95579 | 0.95738 | 0.92083 | 0.95404 | 0.93019 | 0.95413 | 0.94507 | 0.92103 | 0.94061
STT-RAM (opt) | 0.96014 | 0.91453 | 0.9443 | 0.95632 | 0.95951 | 0.92092 | 0.95948 | 0.93564 | 0.96003 | 0.94574 | 0.93546 | 0.94473
Chart: Energy vs. DRAM
| mpmix0 | mpmix1 | mpmix2 | mpmix3 | mpmix4 | mpmix5 | mpmix6 | mpmix7 | mpmix8 | mpmix9 | mpmix10 | Average
ACT+PRE | 0.30175 | 0.27646 | 0.37425 | 0.32119 | 0.33973 | 0.34883 | 0.36197 | 0.2603 | 0.33524 | 0.39385 | 0.32655 | 0.33092
WB | 0.018529 | 0.027397 | 0.013518 | 0.015979 | 0.022233 | 0.018649 | 0.015872 | 0.025826 | 0.01687 | 0.016362 | 0.015008 | 0.018749
RB | 0.01752 | 0.014162 | 0.010281 | 0.018781 | 0.023665 | 0.010148 | 0.024161 | 0.016986 | 0.013315 | 0.012743 | 0.010166 | 0.01563
Kultursay+, “Evaluating STT-RAM as an Energy-Efficient Main Memory Alternative,” ISPASS 2013.

## Slide 100: Other Opportunities with Emerging Technologies
Merging of memory and storage
  e.g., a single interface to manage all data
New applications
  e.g., ultra-fast checkpoint and restore
More robust system design
  e.g., reducing data loss
Processing tightly-coupled with memory
  e.g., enabling efficient search and filtering

## Slide 101: Coordinated Memory and Storage with NVM (I)
The traditional two-level storage model is a bottleneck with NVM
  Volatile data in memory  a load/store interface
  Persistent data in storage  a file system interface
  Problem: Operating system (OS) and file system (FS) code to locate, translate, buffer data become performance and energy bottlenecks with fast NVM stores
Two-Level Store
Processor
and caches
Main Memory
Storage (SSD/HDD)
Virtual memory
Address translation
Load/Store
Operating system
and file system
fopen, fread, fwrite, …
Persistent (e.g., Phase-Change)
Memory

## Slide 102: Coordinated Memory and Storage with NVM (II)
Goal: Unify memory and storage management in a single unit to eliminate wasted work to locate, transfer, and translate data
  Improves both energy and performance
  Simplifies programming model as well
Unified Memory/Storage
Processor
and caches
Persistent (e.g., Phase-Change) Memory
Load/Store
Persistent Memory
Manager
Feedback
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 103: The Persistent Memory Manager (PMM)
Exposes a load/store interface to access persistent data
  Applications can directly access persistent memory  no conversion, translation, location overhead for persistent data
Manages data placement, location, persistence, security
  To get the best of multiple forms of storage
Manages metadata storage and retrieval
  This can lead to overheads that need to be managed
Exposes hooks and interfaces for system software
  To enable better data placement and management decisions
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.
Notes: Let’s take a closer look at the high-level design goals for a Persistent Memory Manager, or PMM.
[click] The most noticeable feature of the PMM – from the system software perspective – is the fact that it exposes a load/store interface to access all persistent data in the system. This means that applications can allocate portions of persistent memory, just as they would allocate portions of volatile DRAM memory in today’s systems.
[click] Of course, with a diverse array of devices managed by a persistent memory, it will be important for the PMM to leverage each of their strengths – and mitigate each of their weaknesses – as much as possible. To this end, the PMM is responsible for managing how volatile and persistent are placed among devices, to ensure data can be efficiently located, persistence guarantees met, and any security rules enforced.
[click] The PMM is also responsible for managing metadata storage and retrieval. We will later evaluate how such overheads affect system performance.
[click] In addition, to achieve the best performance and energy efficiency for the applications running on a system, it will be necessary for the system software to provide hints to the hardware to be used to make more efficient data placement decisions.

## Slide 104: The Persistent Memory Manager (PMM)
PMM uses access and hint information to allocate, locate, migrate and access data in the heterogeneous array of devices
Persistent objects
Notes: And to tie everything together, here is how a persistent memory would operate. Code allocates persistent objects and accesses them using loads and stores – no different than persistent memory in today’s machines. Optionally, the software can provide hints as to the types of access patterns or requirements of the software.
Then, a Persistent Memory Manager uses this access information and software hints to allocate, locate, migrate, and access data among the heterogeneous array of devices present on the system, attempting to strike a balance between application-level guarantees, like persistence and security, and performance and energy efficiency.

## Slide 105: Performance Benefits of a Single-Level Store
~5X
~24X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 106: Energy Benefits of a Single-Level Store
~5X
~16X
Meza+, “A Case for Efficient Hardware-Software Cooperative Management of Storage and Memory,” WEED 2013.

## Slide 107: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
How Can We Do Better?
Summary

## Slide 108: Principles (So Far)
Better cooperation between devices and the system
  Expose more information about devices to upper layers
  More flexible interfaces
Better-than-worst-case design
  Do not optimize for the worst case
  Worst case should not determine the common case
Heterogeneity in design (specialization, asymmetry)
  Enables a more efficient design (No one size fits all)
These principles are coupled

## Slide 109: Agenda
Major Trends Affecting Main Memory
The Memory Scaling Problem and Solution Directions
  New Memory Architectures
  Enabling Emerging Technologies
How Can We Do Better?
Summary

## Slide 110: Summary: Memory Scaling
Memory scaling problems are a critical bottleneck for system performance, efficiency, and usability
New memory architectures
  A lot of hope in fixing DRAM
Enabling emerging NVM technologies
  A lot of hope in hybrid memory systems and single-level stores
System-level memory/storage QoS
  A lot of hope in designing a predictable system
Three principles are essential for scaling
  Software/hardware/device cooperation
  Better-than-worst-case design
  Heterogeneity (specialization, asymmetry)

## Slide 111: Acknowledgments
My current and past students and postdocs
  Rachata Ausavarungnirun, Abhishek Bhowmick, Amirali Boroumand, Rui Cai, Yu Cai, Kevin Chang, Saugata Ghose, Kevin Hsieh, Tyler Huberty, Ben Jaiyen, Samira Khan, Jeremie Kim, Yoongu Kim, Yang Li, Jamie Liu, Lavanya Subramanian, Donghyuk Lee, Yixin Luo, Justin Meza, Gennady Pekhimenko, Vivek Seshadri, Lavanya Subramanian, Nandita Vijaykumar, HanBin Yoon, Jishen Zhao, …
My collaborators at CMU
  Greg Ganger, Phil Gibbons, Mor Harchol-Balter, James Hoe, Mike Kozuch, Ken Mai, Todd Mowry, …
My collaborators elsewhere
  Can Alkan, Chita Das, Sriram Govindan, Norm Jouppi, Mahmut Kandemir, Konrad Lai, Yale Patt, Moinuddin Qureshi, Partha Ranganathan, Bikash Sharma, Kushagra Vaid, Chris Wilkerson, …

## Slide 112: Funding Acknowledgments
NSF
GSRC
SRC
CyLab
AMD, Google, Facebook, HP Labs, Huawei, IBM, Intel, Microsoft, Nvidia, Oracle, Qualcomm, Rambus, Samsung, Seagate, VMware

## Slide 113: Open Source Tools
Rowhammer
  https://github.com/CMU-SAFARI/rowhammer
Ramulator
  https://github.com/CMU-SAFARI/ramulator
MemSim
  https://github.com/CMU-SAFARI/memsim
NOCulator
  https://github.com/CMU-SAFARI/NOCulator
DRAM Error Model
  http://www.ece.cmu.edu/~safari/tools/memerr/index.html
Other open-source software from my group
  https://github.com/CMU-SAFARI/
  http://www.ece.cmu.edu/~safari/tools.html

## Slide 114: Referenced Papers
All are available at
  http://users.ece.cmu.edu/~omutlu/projects.htm
  http://scholar.google.com/citations?user=7XyGUGkAAAAJ&hl=en
A detailed accompanying overview paper
  Onur Mutlu and Lavanya Subramanian, "Research Problems and Opportunities in Memory Systems" Invited Article in Supercomputing Frontiers and Innovations (SUPERFRI), 2015.

## Slide 115: Related Videos and Course Materials
Undergraduate Computer Architecture Course Lecture Videos (2013, 2014, 2015)
Undergraduate Computer Architecture Course Materials (2013, 2014, 2015)
Graduate Computer Architecture Course Materials (Lecture Videos)
Parallel Computer Architecture Course Materials (Lecture Videos)
Memory Systems Short Course Materials
(Lecture Video on Main Memory and DRAM Basics)

## Slide 116: Thank you.
onur@cmu.edu
http://users.ece.cmu.edu/~omutlu/

## Slide 117: Rethinking Memory System Design (for Data-Intensive Computing)
Onur Mutlu
onur@cmu.edu
http://users.ece.cmu.edu/~omutlu/
July 20, 2015
SAMOS Keynote

## Slide 118: Another Talk: NAND Flash Scaling Challenges
Onur Mutlu, "Error Analysis and Management for MLC NAND Flash Memory" Technical talk at Flash Memory Summit 2014 (FMS), Santa Clara, CA, August 2014. Slides (ppt) (pdf)
Cai+, “Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis,” DATE 2012.
Cai+, “Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime,” ICCD 2012.
Cai+, “Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling,” DATE 2013.
Cai+, “Error Analysis and Retention-Aware Error Management for NAND Flash Memory,” Intel Technology Journal 2013.
Cai+, “Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation,” ICCD 2013.
Cai+, “Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories,” SIGMETRICS 2014.
Cai+,”Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery,” HPCA 2015.
Cai+, “Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation,” DSN 2015.
Luo+, “WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management,” MSST 2015.

## Slide 119: Experimental Infrastructure (Flash)
USB Jack
Virtex-II Pro
(USB controller)
Virtex-V FPGA
(NAND Controller)
HAPS-52 Mother Board
USB Daughter Board
NAND Daughter Board
3x-nm
NAND Flash
[Cai+, DATE 2012, ICCD 2012, DATE 2013, ITJ 2013, ICCD 2013, SIGMETRICS 2014, HPCA 2015, DSN 2015, MSST 2015]

## Slide 120: Backup Slides

## Slide 121: Current Research Focus Areas
Research Focus: Computer architecture, HW/SW, bioinformatics
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis & assembly algorithms and architectures
General Purpose GPUs
Heterogeneous
Processors and
Accelerators
Hybrid Main Memory
Persistent Memory/Storage
Broad research
spanning apps, systems, logic
with architecture at the center
Notes: Professor Mutlu’s research focus is all aspects of computer architecture, HW/SW interaction and bioinformatics.
He is looking for students to perform research in these areas.
He and his group, SAFARI, solve fundamental problems spanning:
Memory, memory, memory, storage, interconnects
Parallel architectures, heterogeneous architectures, GP-GPUs
System/architecture interaction, new execution models
Energy efficiency, fault tolerance, hardware security
Genome sequence analysis and assembly
His group does broad research spanning systems to logic with architecture at center

## Slide 122: Some Current Directions and Projects
Rethinking Memory System Design for Data-Intensive Computing
  All aspects of DRAM, Flash Memory, Emerging Technologies
Single-Level Stores: Merging Memory and Storage with Fast NVM
GPUs as First-Class Computing Engines
In-memory Computing: Enabling Near-Data Processing
Predictable Systems: QoS Everywhere in the System
Secure and Easy-to-Program/Manage Memories: DRAM, Flash, NVM
Heterogeneous Systems: Architecting and Exploiting Asymmetry
Efficient and Scalable Interconnects
Genome Sequence Analysis & Assembly: Algorithms and Architectures
Notes: Some concrete current directions his group is exploring are:
Rethinking Memory System Design for Data-Intensive Computing
  Rethinking DRAM, Flash Memory, Emerging Technologies
Single-Level Stores: Merging Memory and Storage with Fast NVM
GP-GPUs as First-Class Computing Engines
In-memory computing
Predictable computing: QoS from the ground up
Secure Memories: DRAM, Flash, NVM
Genome Sequence Analysis and Assembly Algorithms and Architectures

## Slide 123: In-Memory Processing

## Slide 124: A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing
Junwhan Ahn, Sungpack Hong*, Sungjoo Yoo,
Onur Mutlu+, Kiyoung Choi
Seoul National University
*Oracle Labs
+Carnegie Mellon University

## Slide 125: Challenges in Scalable Graph Processing
Challenge 1: How to provide high memory bandwidth to computation units in a practical way?
  Processing-in-memory based on 3D-stacked DRAM
Challenge 2: How to design computation units that efficiently exploit large memory bandwidth?
  Specialized in-order cores called Tesseract cores
    Latency-tolerant programming model
    Graph-processing-specific prefetching schemes

## Slide 126: Tesseract System fo Graph Processing
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)

## Slide 127: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
(with FDP)
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
(with FDP)
Tesseract
32 Tesseract Cores
(32-entry MQ, 4KB PF Buffer)

## Slide 128: Workloads
Five graph processing algorithms
  Average teenage follower
  Conductance
  PageRank
  Single-source shortest path
  Vertex cover
Three real-world large graphs
  ljournal-2008 (social network)
  enwiki-2003 (Wikipedia)
  indochina-0024 (web graph)
  4~7M vertices, 79~194M edges

## Slide 129: Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814

## Slide 130: Memory Energy Consumption
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
-87%

## Slide 131: Conclusion
Revisiting the PIM concept in a new context
  Cost-effective 3D integration of logic and memory
  Graph processing workloads demanding high memory bandwidth
Tesseract: scalable PIM for graph processing
  Many in-order cores in a memory chip
  New message passing mechanism for latency hiding
  New hardware prefetchers for graph processing
  Programming interface that exploits our hardware design
Evaluations demonstrate the benefits of Tesseract
  14x performance improvement & 87% energy reduction
  Scalable: memory-capacity-proportional performance

## Slide 132: PIM-Enabled Instructions: A Low-Overhead, Locality-Aware PIM Architecture
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu+, and Kiyoung Choi
Seoul National University
+Carnegie Mellon University

## Slide 133: Challenges in Processing-in-Memory
DRAM die
Cost-effectiveness
Programming Model
Coherence & VM
DRAM die
Complex Logic
Host Processor
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Host Processor
C
C
In-Memory Processors
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
5
4

## Slide 134: PIM-Enabled Instructions
Our direction: simple PIM operations as ISA extension
  Simple: low-overhead implementation
  ISA extension: No changes to existing programming models
  One more thing: locality-aware dynamic PIM execution
    Adaptation between host-side and memory-side execution
Evaluation highlight
  47% speedup over conventional systems in large inputs
  32% speedup over PIM-only systems in small inputs
  Impact of data locality, energy efficiency, and more…
Session 6A: Memory Systems I (10:20~10:45)

## Slide 135: NVM and Emerging Technologies

## Slide 136: Error Management in MLC NAND Flash
Problem: MLC NAND flash memory reliability/endurance is a key challenge for satisfying future storage systems’ requirements
Our Goals: (1) Build reliable error models for NAND flash memory via experimental characterization, (2) Develop efficient techniques to improve reliability and endurance
This talk provides a “flash” summary of our recent results published in the past 3 years:
  Experimental error and threshold voltage characterization [DATE’12&13]
  Retention-aware error management [ICCD’12]
  Program interference analysis and read reference V prediction [ICCD’13]
  Neighbor-assisted error correction [SIGMETRICS’14]

## Slide 137: Charge vs. Resistive Memories
Charge Memory (e.g., DRAM, Flash)
  Write data by capturing charge Q
  Read data by detecting voltage V
Resistive Memory (e.g., PCM, STT-MRAM, memristors)
  Write data by pulsing current dQ/dt
  Read data by detecting resistance R

## Slide 139: DRAM vs. PCM: An Observation
Row buffers are the same in DRAM and PCM
Row buffer hit latency same in DRAM and PCM
Row buffer miss latency small in DRAM, large in PCM
Accessing the row buffer in PCM is fast
What incurs high latency is the PCM array access  avoid this
CPU
DRAMCtrl
PCM Ctrl
Bank
Bank
Bank
Bank
Row buffer
DRAM Cache
PCM Main Memory
N ns row hit
Fast row miss
N ns row hit
Slow row miss

## Slide 140: Row-Locality-Aware Data Placement
Idea: Cache in DRAM only those rows that
  Frequently cause row buffer conflicts  because row-conflict latency is smaller in DRAM
  Are reused many times  to reduce cache pollution and bandwidth waste
Simplified rule of thumb:
  Streaming accesses: Better to place in PCM
  Other accesses (with some reuse): Better to place in DRAM
Yoon et al., “Row Buffer Locality-Aware Data Placement in Hybrid Memories,” ICCD 2012 Best Paper Award.

## Slide 141: More Detail on New Memory Architectures

## Slide 142: In-DRAM Bitwise AND/OR
Required Operation: Perform a bitwise AND of two rows A and B and store the result in C
R0 – reserved zero row, R1 – reserved one row
D1, D2, D3 – Designated rows for triple activation
RowClone A into D1
RowClone B into D2
RowClone R0 into D3
ACTIVATE D1,D2,D3
RowClone Result into C

## Slide 143: Bitmap Index
Alternative to B-tree and its variants
Efficient for performing range queries and joins
Bitmap 1
Bitmap 2
Bitmap 4
Bitmap 3
age < 18
18 < age < 25
25 < age < 60
age > 60

## Slide 144: Performance Evaluation
Chart: Number of OR bins
| 3.0 | 9.0 | 20.0 | 45.0 | 98.0 | 118.0 | 128.0
Conservative (1 Bank) | 1.24 | 1.2 | 1.21 | 1.22 | 1.23 | 1.23 | 1.23
Aggressive (1 Bank) | 1.26 | 1.24 | 1.26 | 1.27 | 1.28 | 1.28 | 1.28
Conservative (4 Banks) | 1.28 | 1.27 | 1.29 | 1.3 | 1.32 | 1.32 | 1.32
Aggressive (4 Banks) | 1.28 | 1.28 | 1.3 | 1.31 | 1.33 | 1.33 | 1.33

## Slide 145: A Mechanism to Reduce Memory Interference
Memory Channel Partitioning
  Idea: System software maps badly-interfering applications’ pages to different channels [Muralidhara+, MICRO’11]
Separate data of low/high intensity and low/high row-locality applications
Especially effective in reducing interference of threads with “medium” and “heavy” memory intensity
  11% higher performance over existing systems (200 workloads)
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Channel 1
Bank 0
Bank 1
Bank 0
Conventional Page Mapping
Time Units
1
2
3
4
5
Channel Partitioning
Core 0
App A
Core 1
App B
Channel 0
Bank 1
Bank 0
Bank 1
Bank 0
Time Units
1
2
3
4
5
Channel 1

## Slide 146: More on Memory Channel Partitioning
Sai Prashanth Muralidhara, Lavanya Subramanian, Onur Mutlu, Mahmut Kandemir, and Thomas Moscibroda, "Reducing Memory Interference in Multicore Systems via Application-Aware Memory Channel Partitioning" Proceedings of the 44th International Symposium on Microarchitecture (MICRO), Porto Alegre, Brazil, December 2011. Slides (pptx)

## Slide 147: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11] [Ebrahimi+ ISCA’11, MICRO’11] [Ausavarungnirun+, ISCA’12][Subramanian+, HPCA’13] [Subramanian+, ICCD’14]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11, Top Picks ’12]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11, TOCS’12] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10] [Nychis+ SIGCOMM’12]
  QoS-aware data mapping to memory controllers [Muralidhara+ MICRO’11]
  QoS-aware thread scheduling to cores [Das+ HPCA’13]

## Slide 148: QoS-Aware Memory Scheduling
How to schedule requests to provide
  High system performance
  High fairness to applications
  Configurability to system software
Memory controller needs to be aware of threads
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 149: More on DRAM Disturbance Errors
Yoongu Kim, Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee, Donghyuk Lee, Chris Wilkerson, Konrad Lai, and Onur Mutlu, "Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors" Proceedings of the 41st International Symposium on Computer Architecture (ISCA), Minneapolis, MN, June 2014. Slides (pptx) (pdf) Lightning Session Slides (pptx) (pdf) Source Code and Data
Source Code
  https://github.com/CMU-SAFARI/rowhammer

## Slide 150: More on Heterogeneous-Reliability Memory
Yixin Luo, Sriram Govindan, Bikash Sharma, Mark Santaniello, Justin Meza, Aman Kansal, Jie Liu, Badriddine Khessib, Kushagra Vaid, and Onur Mutlu, "Characterizing Application Memory Error Vulnerability to Optimize Data Center Cost via Heterogeneous-Reliability Memory" Proceedings of the 44th Annual IEEE/IFIP International Conference on Dependable Systems and Networks (DSN), Atlanta, GA, June 2014. Slides (pptx) (pdf) Coverage on ZDNet

## Slide 152: How Do We Solve The Problem?
Tolerate it: Make DRAM and controllers more intelligent
  New interfaces, functions, architectures: system-DRAM codesign
Eliminate or minimize it: Replace or (more likely) augment DRAM with a different technology
  New technologies and system-wide rethinking of memory & storage
Embrace it: Design heterogeneous-reliability memories that map error-tolerant data to less reliable portions
  New models for execution and maybe usage
…
Solutions (to memory scaling) require
software/hardware/device cooperation

## Slide 153: More on Memory Scheduling
Lavanya Subramanian, Vivek Seshadri, Yoongu Kim, Ben Jaiyen, and Onur Mutlu, "MISE: Providing Performance Predictability and Improving Fairness in Shared Main Memory Systems" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)
Lavanya Subramanian, Donghyuk Lee, Vivek Seshadri, Harsha Rastogi, and Onur Mutlu, "The Blacklisting Memory Scheduler: Achieving High Performance and Fairness at Low Cost" Proceedings of the 32nd IEEE International Conference on Computer Design (ICCD), Seoul, South Korea, October 2014. Slides (pptx) (pdf)
Yoongu Kim, Michael Papamichael, Onur Mutlu, and Mor Harchol-Balter, "Thread Cluster Memory Scheduling: Exploiting Differences in Memory Access Behavior" Proceedings of the 43rd International Symposium on Microarchitecture (MICRO), pages 65-76, Atlanta, GA, December 2010. Slides (pptx) (pdf)

## Slide 154: Ramulator: A Fast and Extensible DRAM Simulator [IEEE Comp Arch Letters’15]

## Slide 155: Ramulator Motivation
DRAM and Memory Controller landscape is changing
Many new and upcoming standards
Many new controller designs
A fast and easy-to-extend simulator is very much needed

## Slide 156: Ramulator
Provides out-of-the box support for many DRAM standards:
  DDR3/4, LPDDR3/4, GDDR5, WIO1/2, HBM, plus new proposals (SALP, AL-DRAM, TLDRAM, RowClone, and SARP)
~2.5X faster than fastest open-source simulator
Modular and extensible to different standards

## Slide 157: Case Study: Comparison of DRAM Standards
Across 22 workloads, simple CPU model

## Slide 158: Ramulator Paper and Source Code
Yoongu Kim, Weikun Yang, and Onur Mutlu, "Ramulator: A Fast and Extensible DRAM Simulator" IEEE Computer Architecture Letters (CAL), March 2015. [Source Code]
Source code is released under the liberal MIT License
  https://github.com/CMU-SAFARI/ramulator