## Slide 1: Memory Systems and Memory-Centric Computing Systems Part 4: Low-Latency Memory
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
7 July 2019
SAMOS Tutorial

## Slide 2: Four Key Issues in Future Platforms
Fundamentally Secure/Reliable/Safe Architectures
Fundamentally Energy-Efficient Architectures
  Memory-centric (Data-centric) Architectures
Fundamentally Low-Latency Architectures
Architectures for Genomics, Medicine, Health

## Slide 3: Solving the Hardest Problems
Source: http://spectrum.ieee.org/image/MjYzMzAyMg.jpeg

## Slide 4: Maslow’s Hierarchy of Needs, A Third Time
Speed
Speed
Speed
Speed
Speed
Source: https://www.simplypsychology.org/maslow.html
Maslow, “A Theory of Human Motivation,”
Psychological Review, 1943.
Maslow, “Motivation and Personality,”
Book, 1954-1970.

## Slide 5: Challenge and Opportunity for Future
Fundamentally
Low-Latency
Computing Architectures

## Slide 6: Main Memory Latency Lags Behind
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 7: A Closer Look …
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 8: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]

## Slide 9: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 10: The Memory Latency Problem
High memory latency is a significant limiter of system performance and energy-efficiency
It is becoming increasingly so with higher memory contention in multi-core and heterogeneous architectures
  Exacerbating the bandwidth need
  Exacerbating the QoS problem
It increases processor design complexity due to the mechanisms incorporated to tolerate memory latency

## Slide 11: Retrospective: Conventional Latency Tolerance Techniques
Caching [initially by Wilkes, 1965]
  Widely used, simple, effective, but inefficient, passive
  Not all applications/phases exhibit temporal or spatial locality
Prefetching [initially in IBM 360/91, 1967]
  Works well for regular memory access patterns
  Prefetching irregular access patterns is difficult, inaccurate, and hardware-intensive
Multithreading [initially in CDC 6600, 1964]
  Works well if there are multiple threads
  Improving single thread performance using multithreading hardware is an ongoing research effort
Out-of-order execution [initially by Tomasulo, 1967]
  Tolerates cache misses that cannot be prefetched
  Requires extensive hardware resources for tolerating long latencies
None of These
Fundamentally Reduce
Memory Latency

## Slide 12: Runahead Execution

## Slide 13: Runahead Execution Example
Compute
Compute
Compute
Load 1 Miss
Miss 1
Stall
Compute
Load 2 Miss
Miss 2
Stall
Load 1 Hit
Load 2 Hit
Compute
Load 1 Miss
Runahead
Load 2 Miss
Load 2 Hit
Miss 1
Miss 2
Compute
Load 1 Hit
Saved Cycles
Perfect Caches:
Small OoO Instruction Window:
Runahead:

## Slide 14: Effect of Runahead in Sun ROCK
Shailender Chaudhry talk, Aug 2008.

## Slide 15: More on Runahead Execution
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Alternative to Very Large Instruction Windows for Out-of-order Processors" Proceedings of the 9th International Symposium on High-Performance Computer Architecture (HPCA), pages 129-140, Anaheim, CA, February 2003. Slides (pdf)

## Slide 16: More on Runahead Execution (Short)
Onur Mutlu, Jared Stark, Chris Wilkerson, and Yale N. Patt, "Runahead Execution: An Effective Alternative to Large Instruction Windows" IEEE Micro, Special Issue: Micro's Top Picks from Microarchitecture Conferences (MICRO TOP PICKS), Vol. 23, No. 6, pages 20-25, November/December 2003.

## Slide 17: Runahead Readings
Required
  Mutlu et al., “Runahead Execution”, HPCA 2003, Top Picks 2003.
Recommended
  Mutlu et al., “Efficient Runahead Execution: Power-Efficient Memory Latency Tolerance,” ISCA 2005, IEEE Micro Top Picks 2006.
  Mutlu et al., “Address-Value Delta (AVD) Prediction,” MICRO 2005.
  Armstrong et al., “Wrong Path Events,” MICRO 2004.

## Slide 18: Retrospective: Conventional Latency Tolerance Techniques
Caching [initially by Wilkes, 1965]
  Widely used, simple, effective, but inefficient, passive
  Not all applications/phases exhibit temporal or spatial locality
Prefetching [initially in IBM 360/91, 1967]
  Works well for regular memory access patterns
  Prefetching irregular access patterns is difficult, inaccurate, and hardware-intensive
Multithreading [initially in CDC 6600, 1964]
  Works well if there are multiple threads
  Improving single thread performance using multithreading hardware is an ongoing research effort
Out-of-order execution [initially by Tomasulo, 1967]
  Tolerates cache misses that cannot be prefetched
  Requires extensive hardware resources for tolerating long latencies
None of These
Fundamentally Reduce
Memory Latency

## Slide 19: Two Major Sources of Latency Inefficiency
Modern DRAM is not designed for low latency
  Main focus is cost-per-bit (capacity)
Modern DRAM latency is determined by worst case conditions and worst case devices
  Much of memory latency is unnecessary
Our Goal: Reduce Memory Latency at the Source of the Problem

## Slide 20: Truly Reducing Memory Latency

## Slide 21: Two Major Sources of Latency Inefficiency
Modern DRAM is not designed for low latency
  Main focus is cost-per-bit (capacity)
Modern DRAM latency is determined by worst case conditions and worst case devices
  Much of memory latency is unnecessary
Our Goal: Reduce Memory Latency at the Source of the Problem

## Slide 22: Why the Long Memory Latency?
Reason 1: Design of DRAM Micro-architecture
  Goal: Maximize capacity/area, not minimize latency
Reason 2: “One size fits all” approach to latency specification
  Same latency parameters for all temperatures
  Same latency parameters for all DRAM chips
  Same latency parameters for all parts of a DRAM chip
  Same latency parameters for all supply voltage levels
  Same latency parameters for all application data
  …

## Slide 23: Tackling the Fixed Latency Mindset
Reliable operation latency is actually very heterogeneous
  Across temperatures, chips, parts of a chip, voltage levels, …
Idea: Dynamically find out and use the lowest latency one can reliably access a memory location with
  Adaptive-Latency DRAM [HPCA 2015]
  Flexible-Latency DRAM [SIGMETRICS 2016]
  Design-Induced Variation-Aware DRAM [SIGMETRICS 2017]
  Voltron [SIGMETRICS 2017]
  DRAM Latency PUF [HPCA 2018]
  DRAM Latency True Random Number Generator [HPCA 2019]
  ...
We would like to find sources of latency heterogeneity and exploit them to minimize latency (or create other benefits)

## Slide 24: Latency Variation in Memory Chips
High
Low
DRAM Latency
DRAM B
DRAM A
DRAM C
Slow cells
Heterogeneous manufacturing & operating conditions → latency variation in timing parameters

## Slide 25: Why is Latency High?
DRAM latency: Delay as specified in DRAM standards
  Doesn’t reflect true DRAM device latency
Imperfect manufacturing process → latency variation
High standard latency chosen to increase yield
High
Low
DRAM Latency
DRAM A
DRAM B
DRAM C
Manufacturing Variation
Standard
Latency
Notes: To understand the latency problem, we need to go into what defines latency.
DRAM latency is the total amnt of time that the underlying hw operations need <> to retrieve data.
The DRAM standards define a single fixed time for how long these ops should take in every DRAM chip.
However, this defined delay doesn’t actually reflect the latency of the individual DRAMs.
<Timeline illustration>
Because the manufacturing process is imperfect, it introduces variation in the production chips, resulting in latency variation across different chips.
This simple illustartion shows the difference b/w the average latency across 3 different dram chips, to convey the point of latency variation.
It’s important to note that not only does latency variation exists <across> chips, but also <inside> each dram chip itself.
<Blue standard>
Since we don’t want to throw away the chips with high variation, we tolerate them.
The simple way is to <slow> down the acceptable latency so that the majority of chips can all work reliably under this high standard latency.
as we can see, the high standard latency is a result of a trade-off made for higher DRAM production yield.
---
<> Operative word

## Slide 26: What Causes the Long Memory Latency?
Conservative timing margins!
DRAM timing parameters are set to cover the worst case
Worst-case temperatures
  85 degrees vs. common-case
  to enable a wide range of operating conditions
Worst-case devices
  DRAM cell with smallest charge across any acceptable device
  to tolerate process variation at acceptable yield
This leads to large timing margins for the common case

## Slide 27: Understanding and Exploiting Variation in DRAM Latency

## Slide 28: DRAM Characterization Infrastructure
  Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 29: DRAM Characterization Infrastructure
Hasan Hassan et al., SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies, HPCA 2017.
Flexible
Easy to Use (C++ API)
Open-source
github.com/CMU-SAFARI/SoftMC

## Slide 30: SoftMC: Open Source DRAM Infrastructure
https://github.com/CMU-SAFARI/SoftMC

## Slide 31: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer provides multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 32
Latency Reduction Summary of 115 DIMMs
Latency reduction for read & write (55°C)
  Read Latency: 32.7%
  Write Latency: 55.1%
Latency reduction for each timing parameter (55°C)
  Sensing: 17.3%
  Restore: 37.3% (read), 54.8% (write)
  Precharge: 35.2%
Lee+, “Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,” HPCA 2015.

## Slide 33
AL-DRAM: Real System Evaluation
System
  CPU: AMD 4386 ( 8 Cores, 3.1GHz, 8MB LLC)
  DRAM: 4GByte DDR3-1600 (800Mhz Clock)
  OS: Linux
  Storage: 128GByte SSD
Workload
  35 applications from SPEC, STREAM, Parsec, Memcached, Apache, GUPS

## Slide 34
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
1.4%
6.7%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
5.0%
AL-DRAM: Single-Core Evaluation
AL-DRAM improves single-core performance
on a real system
Performance Improvement
Average
Improvement
all-35-workload

## Slide 35
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
AL-DRAM: Multi-Core Evaluation
AL-DRAM provides higher performance on
multi-programmed & multi-threaded workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 36: Reducing Latency Also Reduces Energy
AL-DRAM reduces DRAM power consumption by 5.8%
Major reason: reduction in row activation time

## Slide 37: AL-DRAM: Advantages & Disadvantages
Advantages
+ Simple mechanism to reduce latency
+ Significant system performance and energy benefits
+ Benefits higher at low temperature
+ Low cost, low complexity
Disadvantages
- Need to determine reliable operating latencies for different temperatures and different DIMMs  higher testing cost
(might not be that difficult for low temperatures)

## Slide 38: More on Adaptive-Latency DRAM
Donghyuk Lee, Yoongu Kim, Gennady Pekhimenko, Samira Khan, Vivek Seshadri, Kevin Chang, and Onur Mutlu, "Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)] [Full data sets]

## Slide 39: Different Types of Latency Variation
AL-DRAM exploits latency variation
  Across time (different temperatures)
  Across chips
Is there also latency variation within a chip?
  Across different parts of a chip

## Slide 40: Spatial Locality of Activation Errors
Activation errors are concentrated at certain columns of cells
One DIMM @ tRCD=7.5ns
Notes: This fig is showing the prob. of seeing at least 1 bit error in each cache line from one DIMM under trcd = 7.5ns. The y-axis is the row # (in 000s) and the x-axis is the cl #.
The main observation is that errors exhibit spatial locality. In this DIMM, errors tend to cluster at certain columns of cache lines without errors in the majority of the remaining cl.
This is an imperative observation for our proposed mechanism, which I’ll discuss later.
Next, we investigate the impact of reading different data patterns stored in these cells.

## Slide 41: Heterogeneous Latency within A Chip
Observation: DRAM timing errors (slow DRAM cells) are concentrated on certain regions
Flexible-LatencY (FLY) DRAM
  A software-transparent design that reduces latency
Key idea:
  1) Divide memory into regions of different latencies
  2) Memory controller: Use lower latency for regions without slow cells; higher latency for other regions
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.
Notes: To summarize the observations so far, we find that dram timing errors due to shortened act and pre don’t occur in all cells and they are concentrated at certain regions.
So let’s go back to our second main goal which is on improving latency.
TO achieve this, we propose a software… design, called flex.. Dram or FLY for short, to reduce dram latency.
The key idea is the following:
We divide the dram up into different regions based on a latency variation profile.
Then We enable the mc to use different latency for diff regions.
For regions without slow cells, we are going to run it faster at a much lower latency.
For any region that has slow cells, we are going to operate at a higher latency.

## Slide 42: FLY-DRAM Configurations
Chart: Fraction of Cells
| Baseline (DDR3) | D1 | D2 | D3 | Upper Bound
7.5ns | 0 | 13 | 74 | 99 | 100
10ns | 0 | 87 | 26 | 1 | 0
13ns | 100 | 0 | 0 | 0 | 0
Chart: Fraction of Cells
| Baseline (DDR3) | D1 | D2 | D3 | Upper Bound
7.5ns | 0 | 12 | 93 | 99 | 100
10ns | 0 | 88 | 7 | 1 | 0
13ns | 100 | 0 | 0 | 0 | 0
Profiles of 3 real DIMMs
12%
93%
99%
13%
74%
99%
tRCD
tRP
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.
Notes: We evaluate FLY-DRAM with various configurations.
These 2 figures show the fraction of cells with different latencies for act and pre.
X-axis shows you the configurations that we have.
First, we evaluate a baseline dram system with the standardized latency at 13ns.
Then we use latency profiles that were collected from 3 real DIMMs. The percentage numbers show you the fraction of fast cells in each DIMM.
Note that Darker color means faster latency.
We also evalaute an upperbound configuration that has 100% fast cells under 7.5ns.

## Slide 43: Heterogeneous Latency within A Chip
Chart: 40 Workloads
Baseline (DDR3) | 1
FLY-DRAM (D1) | 1.133
FLY-DRAM (D2) | 1.176
FLY-DRAM (D3) | 1.195
Upper Bound | 1.197
17.6%
19.5%
19.7%
13.3%
Chang+, “Understanding Latency Variation in Modern DRAM Chips: Experimental
Characterization, Analysis, and Optimization",” SIGMETRICS 2016.

## Slide 44: FLY-DRAM: Advantages & Disadvantages
Advantages
+ Reduces latency significantly
+ Exploits significant within-chip latency variation
Disadvantages
- Need to determine reliable operating latencies for different parts of a chip  higher testing cost
- Slightly more complicated controller

## Slide 45: Analysis of Latency Variation in DRAM Chips
Kevin Chang, Abhijith Kashyap, Hasan Hassan, Samira Khan, Kevin Hsieh, Donghyuk Lee, Saugata Ghose, Gennady Pekhimenko, Tianshi Li, and Onur Mutlu, "Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Antibes Juan-Les-Pins, France, June 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 46: Why Is There Spatial Latency Variation Within a Chip?

## Slide 47
Inherently fast
inherently slow
What Is Design-Induced Variation?
slow
fast
slow
fast
Systematic variation in cell access times
caused by the physical organization of DRAM
sense amplifiers
wordline drivers
across row
distance from sense amplifier
across column
distance from wordline driver
Notes: As we described, cells in a mat have different distances from peripheral logic.
Cells in different rows have different distance from the sense amplifiers.
Cells in different columns have different distance from the wordline drivers.
Therefore, some regions are inherently faster than other regions,
and some regions are inherently slower than other regions.
We call this architectural variation.

## Slide 48
DIVA Online Profiling
inherently slow
Profile only slow regions to determine min. latency
 Dynamic & low cost latency optimization
sense amplifier
wordline driver
Design-Induced-Variation-Aware
Notes: We propoe AVA Online profiling.
The key idea is profiling only slow regions to determine latency, leading to low cost online DRAM test.

## Slide 49
inherently slow
DIVA Online Profiling
slow cells
design-induced
variation
process
variation
localized error
random error
online profiling
error-correcting code
Combine error-correcting codes & online profiling
 Reliably reduce DRAM latency
sense amplifier
wordline driver
Design-Induced-Variation-Aware
Notes: However, due to the process variation, some cells are more vulnerable than other cells, as the figure show.
These cells are randomly distributed while cells in the slow regions cause localized error.
To address both type of cells,
We integrate conventional ECC to correct the process variation induced errors.
Therefore, combining ECC and online profiling leads to reliably reducing DRAM latency.

## Slide 50
DIVA-DRAM Reduces Latency
Read
Write
Chart: 
| 55°C | 85°C | 55°C | 85°C | 55°C | 85°C | AL-DRAM | AVA Profiling | AVA Profiling + Shuffling
Latency Reduction | 0.31202 | 0.25527 | 0.35118 | 0.3464 | 0.36569 | 0.358
Latency Reduction
DIVA
DIVA
Chart: 
| 55°C | 85°C | 55°C | 85°C | 55°C | 85°C | AL-DRAM | AVA Profiling | AVA Profiling + Shuffling
Latency Reduction | 0.36561 | 0.27539 | 0.394 | 0.38718 | 0.41294 | 0.40274
DIVA
DIVA
DIVA-DRAM reduces latency more aggressively and uses ECC to correct random slow cells
Notes: The figure compares latency reduction by using AL-DRAM, AVA Profiling, and both AVA Profiling and Shuffling.
As we can, using AVA profiling and shuffling enables more latency reduction compared to AL-DRAM.
This is mainly because ECC corrects the worst cells in a DRAM module, reducing more latency.
Therefore, we conclude that AVA-DRAM reduces latency significantly.

## Slide 51: DIVA-DRAM: Advantages & Disadvantages
Advantages
++ Automatically finds the lowest reliable operating latency at system runtime (lower production-time testing cost)
+ Reduces latency more than prior methods (w/ ECC)
+ Reduces latency at high temperatures as well
Disadvantages
- Requires knowledge of inherently-slow regions
- Requires ECC (Error Correcting Codes)
- Imposes overhead during runtime profiling

## Slide 52: Design-Induced Latency Variation in DRAM
Donghyuk Lee, Samira Khan, Lavanya Subramanian, Saugata Ghose, Rachata Ausavarungnirun, Gennady Pekhimenko, Vivek Seshadri, and Onur Mutlu, "Design-Induced Latency Variation in Modern DRAM Chips: Characterization, Analysis, and Latency Reduction Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 53: Understanding & Exploiting the Voltage-Latency-Reliability Relationship

## Slide 54: High DRAM Power Consumption
Problem: High DRAM (memory) power in today’s systems
>40% in POWER7 (Ware+, HPCA’10)
  >40% in GPU (Paul+, ISCA’15)

## Slide 55: Executive Summary
DRAM (memory) power is significant in today’s systems
  Existing low-voltage DRAM reduces voltage conservatively
Goal: Understand and exploit the reliability and latency behavior of real DRAM chips under aggressive reduced-voltage operation
Key experimental observations:
  Huge voltage margin -- Errors occur beyond some voltage
  Errors exhibit spatial locality
  Higher operation latency mitigates voltage-induced errors
Voltron: A new DRAM energy reduction mechanism
  Reduce DRAM voltage without introducing errors
  Use a regression model to select voltage that does not degrade performance beyond a chosen target  7.3% system energy reduction

## Slide 56: Custom Testing Platform
SoftMC [Hassan+, HPCA’17]: FPGA testing platform to
1) Adjust supply voltage to DRAM modules
2) Schedule DRAM commands to DRAM modules
  Existing systems: DRAM commands not exposed to users
Voltage
controller
DRAM
module
FPGA
https://github.com/CMU-SAFARI/DRAM-Voltage-Study

## Slide 57: Reliability Worsens with Lower Voltage
Nominal Voltage
Min. voltage (Vmin) without errors
Reducing voltage below Vmin causes an increasing number of errors
Errors induced by reduced-voltage operation

## Slide 58: Source of Errors
Chart: Supply Voltage (V)
| 1.35 | 1.2 | 1.1000000000000001 | 1 | 0.9
Activate | 8.6089 | 8.9382 | 10.0798 | 12.0854 | 16.1766
Precharge | 7.389 | 8.496 | 9.916 | 12.711 | 19.572
Detailed circuit simulations (SPICE) of a DRAM cell array to model the behavior of DRAM operations
Circuit model
Nominal Voltage
https://github.com/CMU-SAFARI/DRAM-Voltage-Study
Reliable low-voltage operation requires higher latency

## Slide 59: Higher Access Latency  Fewer Errors
Measured minimum latency that does not cause errors in DRAM modules
Lower bound of latency as our latency adjustment granularity is 2.5ns
Measured Minimum Activate Latency (ns)
8
10
12
14
100% of modules
40% of modules
DRAM requires longer latency to access data without errors at lower voltage
Distribution of latency in the total population

## Slide 60: Spatial Locality of Errors
A module under 1.175V (12% voltage reduction)
Errors concentrate in certain regions

## Slide 61: Voltron Overview
How do we predict performance loss due to increased latency under low DRAM voltage?
Voltron
User specifies the performance loss target
Select the minimum DRAM voltage without violating the target

## Slide 62: Linear Model to Predict Performance
Voltron
User specifies the performance loss target
Select the minimum DRAM voltage without violating the target
Linear regression model
Application’s characteristics
[1.3V, 1.25V, …]
DRAM Voltage
[-1%, -3%, …]
Predicted performance loss
Min.
Voltage
Target
Final Voltage

## Slide 63: Energy Savings with Bounded Performance
Chart: Memory Intensity
| Low | High
MemDVFS | 1.4 | 0.4
Voltron | 3.2 | 7
Chart: Memory Intensity
| Low | High
MemDVFS | -2.7 | -2.1
Voltron | -1.6 | -1.8
Performance Target
[David+, ICAC’11]
More savings for high bandwidth applications
Meets performance target
7.3%
3.2%
-1.6%
-1.8%

## Slide 64: Voltron: Advantages & Disadvantages
Advantages
+ Can trade-off between voltage and latency to improve energy or performance
+ Can exploit the high voltage margin present in DRAM
Disadvantages
- Requires finding the reliable operating voltage for each chip  higher testing cost

## Slide 65: Analysis of Latency-Voltage in DRAM Chips
Kevin Chang, A. Giray Yaglikci, Saugata Ghose, Aditya Agrawal, Niladrish Chatterjee, Abhijith Kashyap, Donghyuk Lee, Mike O'Connor, Hasan Hassan, and Onur Mutlu, "Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Urbana-Champaign, IL, USA, June 2017.

## Slide 66: And, What If …
… we can sacrifice reliability of some data to access it with even lower latency?

## Slide 67: The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern Commodity DRAM Devices
Jeremie S. Kim Minesh Patel
Hasan Hassan Onur Mutlu
Notes: Hello, my name is Jeremie Kim and I will be talking about the DRAM Latency PUF.

## Slide 68: Motivation
A PUF is function that generates a signature unique to a given device
Used in a Challenge-Response Protocol
  Each device generates a unique PUF response depending the inputs
  A trusted server authenticates a device if it generates the expected PUF response
Notes: [CLICK] A PUF is a function that generates a signature that is unique to a given device. [CLICK] PUFs are often used in a challenge-response protocol where [CLICK] a trusted server issues a set of input parameters to a device, and the device generates the PUF response depending on the input parameters. [CLICK] The trusted server then receives the PUF response and can authenticate the device.

## Slide 69: DRAM Latency Characterization of 223 LPDDR4 DRAM Devices
Latency failures come from accessing DRAM with reduced timing parameters.
Key Observations:
  A cell’s latency failure probability is determined by random process variation
  Latency failure patterns are repeatable and unique to a device
Notes: In this work, we show results from a detailed experimental characterization of 223 state-of-the-art LPDDR4 DRAM devices. [CLICK] We characterize DRAM latency by observing the effects of accessing DRAM with DRAM timing parameters reduced below manufacturer-recommended values.
[CLICK] We make two key observations. [CLICK] first, a cell’s probability to fail, when accessed with reduced timing parameters, is directly correlated with random variations that arise from process manufacturing. [CLICK] secondly, We note that these error patterns from inducing DRAM latency errors are unique to a device and highly repeatable.

## Slide 70: DRAM Latency PUF Key Idea
Row Decoder
High % chance to fail with reduced tRCD
Low % chance to fail with reduced tRCD
SA
SA
SA
SA
SA
SA
SA
Notes: Here is a cartoon showing the manufacturing variation across a region of DRAM. When accessed with a reduced timing parameter, [CLICK] some cells have a high percentage chance of failing, while others [CLICK] have a low percentage chance of failing.

## Slide 71: DRAM Accesses and Failures
wordline
capacitor
access
transistor
bitline
SA
Vdd
0.5 Vdd
Bitline Voltage
Time
Ready to Access
Voltage Level
tRCD
Process variation during manufacturing leads to cells having unique characteristics
Vmin
ACTIVATE
SA Enable
READ
Bitline Charge Sharing
Notes: [CLICK] A DRAM cell holds its charge in a capacitor and gets read out by the sense amplifier via the bitline. [CLICK][CLICK] Initially the bitline is kept at Vdd/2. [CLICK] When the wordline is driven high or activated, [CLICK] the capacitor begins to share charge with the bitline. The sense amplifier is then enabled and [CLICK] the voltage differential on the bitline is amplified to an I/O readable value. [CLICK] In order to ensure correctness of operation, the memory controller can only read data tRCD time after the activation. [CLICK] We could read this data earlier, when it reaches a readable voltage threshold, [CLICK] but other cells, that are weaker due to process variation, might fail. [CLICK]

## Slide 72: DRAM Accesses and Failures
wordline
capacitor
access
transistor
bitline
SA
Vdd
0.5 Vdd
Bitline Voltage
Time
Ready to Access
Voltage Level
tRCD
Vmin
ACTIVATE
SA Enable
READ
weaker cells have a higher probability to fail
Notes: Our method of inducing latency errors is to [CLICK] reduce tRCD below manufacturer-recommended values. Cells that are read when their bitline’s voltage is lower than the threshold, have a probability of failure. This probability increases as you read further below the voltage threshold.

## Slide 73: The DRAM Latency PUF Evaluation
We generate PUF responses using latency errors in a region of DRAM
The latency error patterns satisfy PUF requirements
The DRAM Latency PUF generates PUF responses in 88.2ms
Notes: [CLICK] The DRAM latency PUF generates a PUF response by inducing latency errors in a region of DRAM. [CLICK] We find that the error patterns from latency errors in a DRAM region satisfy the requirements for an effective PUF quite well. [CLICK] The DRAM latency PUF can generate a PUF response in 88.2ms.

## Slide 74: Results
DL-PUF is orders of magnitude faster than prior DRAM PUFs & temperature independent
Notes: [CLICK] We show by direct comparison that this is orders of magnitudes faster than the previous best DRAM PUF.

## Slide 75: The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern Commodity DRAM Devices
Jeremie S. Kim Minesh Patel
Hasan Hassan Onur Mutlu
QR Code for the paper
https://people.inf.ethz.ch/omutlu/pub/dram-latency-puf_hpca18.pdf
Notes: Please come to my talk at HPCA 2018, if you would like to learn more or have any questions. Thank you very much.

## Slide 76: DRAM Latency PUFs
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "The DRAM Latency PUF: Quickly Evaluating Physical Unclonable Functions by Exploiting the Latency-Reliability Tradeoff in Modern DRAM Devices" Proceedings of the 24th International Symposium on High-Performance Computer Architecture (HPCA), Vienna, Austria, February 2018. [Lightning Talk Video] [Slides (pptx) (pdf)] [Lightning Session Slides (pptx) (pdf)]

## Slide 77: D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput
Jeremie S. Kim Minesh Patel
Hasan Hassan Lois Orosa Onur Mutlu
HPCA 2019

## Slide 78: DRAM Latency Characterization of 282 LPDDR4 DRAM Devices
Latency failures come from accessing DRAM with reduced timing parameters.
Key Observations:
  A cell’s latency failure probability is determined by random process variation
  Some cells fail randomly
Notes: In this work, we show results from a detailed experimental characterization of 282 state-of-the-art LPDDR4 DRAM devices. [CLICK] We characterize DRAM latency by observing the effects of accessing DRAM with DRAM timing parameters reduced below manufacturer-recommended values.
[CLICK] We make two key observations. [CLICK] first, a cell’s probability to fail, when accessed with reduced timing parameters, is directly correlated with random variations that arise from process manufacturing. [CLICK] secondly, We note that some cells fail randomly when accessed with a reduced tRCD.

## Slide 79: D-RaNGe Key Idea
Row Decoder
High % chance to fail with reduced tRCD
Low % chance to fail with reduced tRCD
SA
SA
SA
SA
SA
SA
SA
Fails randomly
with reduced tRCD
Notes: Here is a cartoon showing the manufacturing variation across a region of DRAM. When accessed with a reduced timing parameter, [CLICK] some cells have a high percentage chance of failing, while others [CLICK] have a low percentage chance of failing. [CLICK} Some cells fail randomly when accessed with a reduced tRCD.

## Slide 80: D-RaNGe Key Idea
Row Decoder
High % chance to fail with reduced tRCD
Low % chance to fail with reduced tRCD
SA
SA
SA
SA
SA
SA
SA
Fails randomly
with reduced tRCD
We refer to cells that fail randomly
when accessed with a reduced tRCD
as RNG cells
Notes: We refer to cells that fail randomly when accessed with a reduced tRCD as RNG cells

## Slide 81: Our D-RaNGe Evaluation
We generate random values by repeatedly accessing RNG cells and aggregating the data read
The random data satisfies the NIST statistical test suite for randomness
The D-RaNGE generates random numbers
  Throughput: 717.4 Mb/s
  Latency: 64 bits in <1us
  Power: 4.4 nJ/bit

## Slide 82: D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput
Jeremie S. Kim Minesh Patel
Hasan Hassan Lois Orosa Onur Mutlu
HPCA 2019

## Slide 83: DRAM Latency True Random Number Generator
Jeremie S. Kim, Minesh Patel, Hasan Hassan, Lois Orosa, and Onur Mutlu, "D-RaNGe: Using Commodity DRAM Devices to Generate True Random Numbers with Low Latency and High Throughput" Proceedings of the 25th International Symposium on High-Performance Computer Architecture (HPCA), Washington, DC, USA, February 2019.

## Slide 84: Other Ideas on Reducing DRAM Latency

## Slide 85: Solar-DRAM: Exploiting Spatial Variation
Jeremie S. Kim, Minesh Patel, Hasan Hassan, and Onur Mutlu, "Solar-DRAM: Reducing DRAM Access Latency by Exploiting the Variation in Local Bitlines" Proceedings of the 36th IEEE International Conference on Computer Design (ICCD), Orlando, FL, USA, October 2018.

## Slide 86: ChargeCache: Exploiting Access Patterns
Hasan Hassan, Gennady Pekhimenko, Nandita Vijaykumar, Vivek Seshadri, Donghyuk Lee, Oguz Ergin, and Onur Mutlu, "ChargeCache: Reducing DRAM Latency by Exploiting Row Access Locality" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 87: Reducing Refresh Latency
Anup Das, Hasan Hassan, and Onur Mutlu, "VRL-DRAM: Improving DRAM Performance via Variable Refresh Latency" Proceedings of the 55th Design Automation Conference (DAC), San Francisco, CA, USA, June 2018.

## Slide 88: Why the Long Memory Latency?
Reason 1: Design of DRAM Micro-architecture
  Goal: Maximize capacity/area, not minimize latency
Reason 2: “One size fits all” approach to latency specification
  Same latency parameters for all temperatures
  Same latency parameters for all DRAM chips
  Same latency parameters for all parts of a DRAM chip
  Same latency parameters for all supply voltage levels
  Same latency parameters for all application data
  …

## Slide 89: Tiered-Latency DRAM
Donghyuk Lee, Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian, and Onur Mutlu, "Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)

## Slide 90: LISA: Low-cost Inter-linked Subarrays
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 91: Tiered Latency DRAM

## Slide 92: What Causes the Long Latency?
DRAM Latency = Subarray Latency + I/O Latency
DRAM Chip
channel
cell array
I/O
DRAM Chip
channel
I/O
subarray
DRAM Latency = Subarray Latency + I/O Latency
Dominant
Subarray
I/O
Notes: To understand what causes the long latency, let me take a look at the DRAM organization.
DRAM consists of two components, the cell array and the I/O circuitry. The cell array consists of multiple subarrays.
To read from a DRAM chip, the data is first accessed from the subarray and then the data is transferred over the channel by the I/O circuitry.
So, the DRAM latency is the sum of the subarray latency and the I/O latency.
We observed that the subarray latency is much higher than the I/O latency.
As a result, subarray is the dominant source of the DRAM latency as we explained in the paper.

## Slide 93: Why is the Subarray So Slow?
Subarray
row decoder
sense amplifier
capacitor
access
transistor
wordline
bitline
Cell
large sense amplifier
bitline: 512 cells
cell
Long bitline
  Amortizes sense amplifier cost  Small area
  Large bitline capacitance  High latency & power
sense amplifier
row decoder
Notes: The cell’s capacitor is small and can store only a small amount of charge.
That is why a subarray also has sense-amplifiers, which are specialized circuits that can detect the small amount of charge.
Unfortunately, a sense-amplifier size is about *100* times the cell size.
So, to amortize the area of the sense-amplifiers,
hundreds of cells share the same sense-amplifier through a long bitline.
However, a long bitline has a large capacitance that increases latency and power consumption.
Therefore, the long bitline is one of the dominant sources of high latency and high power consumption.
To understand why the subarray is so slow,
let me take a look at the subarray organization.

## Slide 94: Trade-Off: Area (Die Size) vs. Latency
Faster
Smaller
Short Bitline
Long Bitline
Trade-Off: Area vs. Latency
Notes: A naïve way to reduce the DRAM latency is to have short bitlines that have lower latency.
Unfortunately, short bitlines significantly increase the DRAM area.
Therefore, the bitline length exposes an important trade-off between area and latency.

## Slide 95: Trade-Off: Area (Die Size) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.617764350044659 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Commodity DRAM
Long Bitline
Cheaper
Faster
Fancy DRAM
Short Bitline
GOAL
Notes: This figure shows the trade-off between DRAM area and latency as we change the bitline length.
Y-axis is the normalized DRAM area compared to a DRAM using 512 cells/bitline. A lower value is cheaper.
X-axis shows the latency in terms of tRC, an important DRAM timing constraint. A lower value is faster.
Commodity DRAM chips use long bitlines to minimize area cost. On the other hand, shorter bitlines achieve lower latency at higher cost.
Our goal is to achieve the best of both worlds: low latency and low area cost.

## Slide 96: Approximating the Best of Both Worlds
Short Bitline
Low Latency
Long Bitline
Small Area
Long Bitline
Low Latency
Short Bitline
Our Proposal
Small Area
Short Bitline  Fast
Need Isolation
Add Isolation Transistors
High Latency
Large Area
Notes: To sum up, both long and short bitline do not achieve small area and low latency.
Long bitline has small area but has high latency while short bitline has low latency but has large area.
To achieve the best of both worlds, we first start from long bitline, which has small area.
After that, to achieve the low latency of short bitline, we divide the long bitline into two smaller segments.
The bitline length of the segment nearby the sense-amplifier is same as the length of short bitline.
Therefore, the latency of the segment is as low as the latency of the short bitline.
To isolate this fast segment from the other segment, we add isolation transistors that selectively connect the two segments.

## Slide 97: Approximating the Best of Both Worlds
Low Latency
Our Proposal
Small Area
Long Bitline
Small Area
Long Bitline
High Latency
Short Bitline
Low Latency
Short Bitline
Large Area
Tiered-Latency DRAM
Low Latency
Small area using long bitline
Notes: This way, our proposed approach achieves small area and low latency.
We call this new DRAM architecture as Tiered-Latency DRAM

## Slide 98: Commodity DRAM vs. TL-DRAM [HPCA 2013]
Chart: 
| commodity DRAM | near segment | far segment
Normalized Power Consumption | 1 | 0.49 | 1.49
Chart: 
| commodity DRAM | near segment | far segment
Latency | 1 | 0.56 | 1.23
Latency
Power
  –56%
  +23%
  –51%
  +49%
DRAM Latency (tRC)
DRAM Power
DRAM Area Overhead
  ~3%: mainly due to the isolation transistors
  TL-DRAM
  Commodity DRAM
  Near Far
  Commodity DRAM
  Near Far
  TL-DRAM
  (52.5ns)
Notes: This figure compares the latency.
Y-axis is normalized latency.
Compared to commodity DRAM, TL-DRAM’s near segment has 56% lower latency, while the far segment has 23% higher latency.
The right figure compares the power.
Y-axis is normalized power.
Compared to commodity DRAM, TL-DRAM’s near segment has 51% lower power consumption and the far segment has 49% higher power consumption.
Lastly, mainly due to the isolation transistor, Tiered-latency DRAM increases the die-size by about 3%.

## Slide 99: Trade-Off: Area (Die-Area) vs. Latency
Chart: Latency (ns)
| 23.10725021132788 | 24.617764350044659 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Cheaper
Faster
Near Segment
Far Segment
GOAL
Notes: Again, the figure shows the trade-off between area and latency in existing DRAM.
Unlike existing DRAM, TL-DRAM achieves low latency using the near segment while increasing the area by only 3%.
Although the far segment has higher latency than commodity DRAM, we show that efficient use of the near segment enables TL-DRAM to achieve high system performance.

## Slide 100: Leveraging Tiered-Latency DRAM
TL-DRAM is a substrate that can be leveraged by the hardware and/or software
Many potential uses
  Use near segment as hardware-managed inclusive cache to far segment
  Use near segment as hardware-managed exclusive cache to far segment
  Profile-based page mapping by operating system
  Simply replace DRAM with TL-DRAM
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: There are multiple ways to leverage the TL-DRAM substrate by hardware or software.
In this slide, I describe many such ways.
First, the near segment can be used as a hardware-managed inclusive cache to the far segment.
Second, the near segment can be used as a hardware-managed exclusive cache to the far segment.
Third, the operating system can intelligently allocate frequently-accessed pages to the near segment.
Forth mechanism is to simple replace DRAM with TL-DRAM without any near segment handling
While our paper provides detailed explanations and evaluations of first three mechanism,
in this talk, we will focus on the first approach, which is to use the near segment as a hardware managed cache for the far segment.

## Slide 101: Near Segment as Hardware-Managed Cache
subarray
TL-DRAM
I/O
cache
main
memory
Challenge 1: How to efficiently migrate a row between segments?
Challenge 2: How to efficiently manage the cache?
far segment
near segment
sense amplifier
channel
Notes: This diagram shows TL-DRAM organization.
Each subarray consists of the sense amplifier, near segment and far segment.
In this particular approach, only the far segment capacity is exposed to the operating system and the memory controller caches the frequently accessed rows in each subarray to the corresponding near segment.
This approach has two challenges.
First, how to migrate a row between segments efficiently?
Second, how to manage the near segment cache efficiently?
Let me first address first challenge.

## Slide 102: Performance & Power Consumption
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Performance Improvement | 1.124 | 1.115 | 1.107
Chart: 
| 1 (1-ch) | 2 (2-ch) | 4 (4-ch)
Power Reduction | 0.769 | 0.755 | 0.737
11.5%
Normalized Performance
Core-Count (Channel)
Normalized Power
Core-Count (Channel)
10.7%
12.4%
–23%
–24%
–26%
Using near segment as a cache improves performance and reduces power consumption
Lee+, “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
Notes: This figure shows the IPC improvement of our three caching mechanisms over commodity DRAM.
All of them improve performance and benefit-based caching shows maximum performance improvement by 12.7%.
The right figure shows the normalized power reduction of our three caching mechanisms over commodity DRAM.
All of them reduce power consumption and benefit-based caching shows maximum power reduction by 23%.
Therefore, using near segment as a cache improves performance and reduces power consumption at the cost of 3% area overhead.

## Slide 103: More on TL-DRAM
Donghyuk Lee, Yoongu Kim, Vivek Seshadri, Jamie Liu, Lavanya Subramanian, and Onur Mutlu, "Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture" Proceedings of the 19th International Symposium on High-Performance Computer Architecture (HPCA), Shenzhen, China, February 2013. Slides (pptx)

## Slide 104: LISA: Low-Cost Inter-Linked Subarrays [HPCA 2016]

## Slide 105: Problem: Inefficient Bulk Data Movement
Bulk data movement is a key operation in many applications
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+ ISCA’15]
Memory Controller
CPU
Memory
Channel
dst
src
Long latency and high energy
LLC
Core
Core
Core
Core
64 bits

## Slide 106: Moving Data Inside DRAM?
DRAM cell
Subarray 1
Subarray 2
Subarray 3
Subarray N
…
Internal Data Bus (64b)
8Kb
512 rows
Bank
Bank
Bank
Bank
DRAM
…
Low connectivity in DRAM is the fundamental bottleneck for bulk data movement
Goal: Provide a new substrate to enable wide connectivity between subarrays

## Slide 107: Key Idea and Applications
Low-cost Inter-linked subarrays (LISA)
  Fast bulk data movement between subarrays
  Wide datapath via isolation transistors: 0.8% DRAM chip area
LISA is a versatile substrate → new applications
Subarray 1
Subarray 2
…
  Fast bulk data copy: Copy latency 1.363ms→0.148ms (9.2x) → 66% speedup, -55% DRAM energy
  In-DRAM caching: Hot data access latency 48.7ns→21.5ns (2.2x) → 5% speedup
  Fast precharge: Precharge latency 13.1ns→5.0ns (2.6x) → 8% speedup

## Slide 108: 3. Linked Precharge (LIP)
Problem: The precharge time is limited by the strength of one precharge unit
Linked Precharge (LIP): LISA precharges a subarray using multiple precharge units
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
Precharging
S
P
S
P
S
P
S
P
Activated row
on
on
on
Linked Precharging
Conventional DRAM
LISA DRAM
Reduces precharge latency by 2.6x
(43% guardband)

## Slide 109: More on LISA
Kevin K. Chang, Prashant J. Nair, Saugata Ghose, Donghyuk Lee, Moinuddin K. Qureshi, and Onur Mutlu, "Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM" Proceedings of the 22nd International Symposium on High-Performance Computer Architecture (HPCA), Barcelona, Spain, March 2016. [Slides (pptx) (pdf)] [Source Code]

## Slide 110: CROW: The Copy Row Substrate [ISCA 2019]

## Slide 111: Challenges of DRAM Scaling
access latency
refresh overhead
exposure to vulnerabilities
1
2
3
Notes: DRAM offers high memory capacity at low cost.
However, process technology scaling introduces three key challenges to DRAM [CLICK]
First, high DRAM access latency is a bottleneck for improving system performance and energy efficiency. [CLICK]
Second, as the number of cells in a DRAM chip increase, DRAM refresh overheads incur more performance and energy overheads. [CLICK]
Third, as process technology shrinks, DRAM cells become smaller and get closer to each other. The increasing interference between cells exposes DRAM to vulnerabilities such as RowHammer, which reduce DRAM reliability.

## Slide 112: Conventional DRAM
DRAM Subarray
sense amplifier
Notes: Conventional DRAM chip is composed of multiple subarrays. DRAM cells in a subarray are organized as two-dimensional array.
To access a cell, a DRAM row has to be activated. [CLICK] A row activation results in loading the row’s data into the sense amplifiers, where read and write operations can be performed.

## Slide 113: Copy Row DRAM (CROW)
Row copy
Multiple row activation
DRAM Subarray
sense amplifier
Notes: To address the scaling challenges of conventional DRAM, we propose a flexible substrate which we call CROW.
CROW slightly modifies the DRAM subarray by introducing copy rows in addition to the regular rows in conventional DRAM. The copy rows have their own address decoders and they can be activated independently from the regular rows.
The CROW substrate enables two key operations. [CLICK]
First, it enables duplicating an entire regular row to a copy row within the subarray. This operation is simply performed by following a regular row activation with a copy row activation. [CLICK]
Second, CROW enables simultaneously activating a regular row and a copy row. If the two rows contain the same data, this operation results in low latency activation. This is because two rows share more charge with the sense amplifiers and as a result the sense amplifiers operate faster.

## Slide 114: Use Cases of CROW
CROW-cache
  reduces access latency
CROW-ref
  reduces DRAM refresh overhead
A mechanism for protecting against RowHammer
weak
strong
Notes: The CROW substrate is flexible and can be used to enable a variety of mechanisms.
In this work, we discuss and evaluate two mechanisms. First, [CLICK] CROW-cache enables low-latency access to the most recently activated regular rows in every subarray. To do so, [CLICK] CROW-cache
makes a copy of the activated regular row into an available copy row. During a subsequent access to the same regular row, [CLICK] CROW-cache simultaneously activates both the regular and copy row to reduce activation latency.
[CLICK]
Second, CROW-ref mitigates DRAM refresh overhead by avoiding storing any data in retention-weak rows such that the entire DRAM chip can use a longer refresh interval. [CLICK] CROW-ref simply remaps weak regular DRAM rows to strong copy rows and the memory controller activates the corresponding copy row instead of the weak regular row.
Please come to my talk to learn more about these mechanisms.
[CLICK]
In the talk, we will also briefly discuss a third mechanism for mitigating RowHammer errors.
We hope future work exploits CROW to devise more use cases.

## Slide 115: Key Results
  CROW-cache + CROW-ref
    20% speedup
    22% less DRAM energy
  Hardware Overhead
    0.5% DRAM chip area
    1.6% DRAM capacity
    11.3 KiB memory controller storage
Notes: CROW-cache and CROW-ref are complementary to each other. Averaged across 20 four-core memory intensive workloads, the combination of CROW-cache and CROW-ref improves performance by 20.0% and reduces DRAM energy by 22%.
[CLICK]
CROW provides such performance and energy benefits with a small hardware overhead in the DRAM chip and the memory controller.

## Slide 116: More on CROW
Hasan Hassan, Minesh Patel, Jeremie S. Kim, A. Giray Yaglikci, Nandita Vijaykumar, Nika Mansourighiasi, Saugata Ghose, and Onur Mutlu, "CROW: A Low-Cost Substrate for Improving DRAM Performance, Energy Efficiency, and Reliability" Proceedings of the 46th International Symposium on Computer Architecture (ISCA), Phoenix, AZ, USA, June 2019.

## Slide 117: SALP: Reducing DRAM Bank Conflict Impact
Kim, Seshadri, Lee, Liu, Mutlu
A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM
ISCA 2012.

## Slide 118: SALP: Problem, Goal, Observations
Problem: Bank conflicts are costly for performance and energy
  serialized requests, wasted energy (thrashing of row buffer, busy wait)
Goal: Reduce bank conflicts without adding more banks (low cost)
Observation 1: A DRAM bank is divided into subarrays and each subarray has its own local row buffer

## Slide 119: SALP: Key Ideas
Observation 2: Subarrays are mostly independent
  Except when sharing global structures to reduce cost
Key Idea of SALP: Minimally reduce sharing of global structures
Reduce the sharing of …
Global decoder  Enables almost parallel access to subarrays
Global row buffer  Utilizes multiple local row buffers

## Slide 120: SALP: Reduce Sharing of Global Decoder
Local row-buffer
Local row-buffer
Global row-buffer
···
Global Decoder
Latch
Latch
Latch
Instead of a global latch, have per-subarray latches

## Slide 121: SALP: Reduce Sharing of Global Row-Buffer
Wire
Global bitlines
Global row-buffer
Local row-buffer
Local row-buffer
Switch
Switch
READ
READ
D
D
D
D
Selectively connect local row-buffers to global row-buffer using a Designated single-bit latch

## Slide 122: SALP: Baseline Bank Organization
Local row-buffer
Local row-buffer
Global row-buffer
Global Decoder
Global
bitlines
Latch

## Slide 123: SALP: Proposed Bank Organization
Local row-buffer
Local row-buffer
Global row-buffer
Global Decoder
Latch
Latch
D
D
Global
bitlines
Overhead of SALP in DRAM chip: 0.15%
1. Global latch  per-subarray local latches
2. Designated bit latches and wire to selectively enable a subarray

## Slide 124: SALP: Results
Wide variety of systems with different #channels, banks, ranks, subarrays
Server, streaming, random-access, SPEC workloads
Dynamic DRAM energy reduction: 19%
  DRAM row hit rate improvement: 13%
System performance improvement: 17%
  Within 3% of ideal (all independent banks)
DRAM die area overhead: 0.15%
  vs. 36% overhead of independent banks

## Slide 125: More on SALP
Yoongu Kim, Vivek Seshadri, Donghyuk Lee, Jamie Liu, and Onur Mutlu, "A Case for Exploiting Subarray-Level Parallelism (SALP) in DRAM" Proceedings of the 39th International Symposium on Computer Architecture (ISCA), Portland, OR, June 2012. Slides (pptx)

## Slide 126: More on SALP

## Slide 127: More on SALP
http://www.cs.utah.edu/thememoryforum/kang_slides.pdf

## Slide 128: More on SALP
http://www.cs.utah.edu/thememoryforum/kang_slides.pdf

## Slide 129: Summary: Low-Latency Memory

## Slide 130: Summary: Tackling Long Memory Latency
Reason 1: Design of DRAM Micro-architecture
  Goal: Maximize capacity/area, not minimize latency
Reason 2: “One size fits all” approach to latency specification
  Same latency parameters for all temperatures
  Same latency parameters for all DRAM chips
  Same latency parameters for all parts of a DRAM chip
  Same latency parameters for all supply voltage levels
  Same latency parameters for all application data
  …

## Slide 131: Challenge and Opportunity for Future
Fundamentally
Low-Latency
Computing Architectures

## Slide 132: One Important Takeaway
Main Memory Needs
Intelligent Controllers

## Slide 133: On DRAM Power Consumption

## Slide 134: VAMPIRE DRAM Power Model
Saugata Ghose, A. Giray Yaglikci, Raghav Gupta, Donghyuk Lee, Kais Kudrolli, William X. Liu, Hasan Hassan, Kevin K. Chang, Niladrish Chatterjee, Aditya Agrawal, Mike O'Connor, and Onur Mutlu, "What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Irvine, CA, USA, June 2018. [Abstract]

## Slide 135: More Motivation to Reduce Memory Latency

## Slide 136: Workload-DRAM Interaction Analysis
Saugata Ghose, Tianshi Li, Nastaran Hajinazar, Damla Senol Cali, and Onur Mutlu, "Demystifying Workload–DRAM Interactions: An Experimental Study" Proceedings of the ACM International Conference on Measurement and Modeling of Computer Systems (SIGMETRICS), Phoenix, AZ, USA, June 2019. [Preliminary arXiv Version] [Abstract] [Slides (pptx) (pdf)]

## Slide 137: Memory Systems and Memory-Centric Computing Systems Part 4: Low-Latency Memory
Prof. Onur Mutlu
omutlu@gmail.com
https://people.inf.ethz.ch/omutlu
7 July 2019
SAMOS Tutorial