## Slide 1: Memory Systems in the Many-Core Era: Some Challenges and Solution Directions
Onur Mutlu
onur@cmu.edu
June 5, 2011
ISMM/MSPC

## Slide 2: Modern Memory System: A Shared Resource

## Slide 3: The Memory System
The memory system is a fundamental performance and power bottleneck in almost all computing systems: server, mobile, embedded, desktop, sensor
The memory system must scale (in size, performance, efficiency, cost) to maintain performance and technology scaling
Recent technology, architecture, and application trends lead to new requirements from the memory system:
  Scalability (technology and algorithm)
  Fairness and QoS-awareness
  Energy/power efficiency

## Slide 4: Agenda
Technology, Application, Architecture Trends
Requirements from the Memory Hierarchy
Research Challenges and Solution Directions
  Main Memory Scalability
  QoS support: Inter-thread/application interference
Summary

## Slide 5: Technology Trends
DRAM does not scale well beyond N nm [ITRS 2009, 2010]
  Memory scaling benefits: density, capacity, cost
Energy/power already key design limiters
  Memory hierarchy responsible for a large fraction of power
    IBM servers: ~50% energy spent in off-chip memory hierarchy [Lefurgy+, IEEE Computer 2003]
    DRAM consumes power when idle and needs periodic refresh
More transistors (cores) on chip
Pin bandwidth not increasing as fast as number of transistors
  Memory is the major shared resource among cores
  More pressure on the memory hierarchy

## Slide 6: Application Trends
Many different threads/applications/virtual-machines (will) concurrently share the memory system
  Cloud computing/servers: Many workloads consolidated on-chip to improve efficiency
  GP-GPU, CPU+GPU, accelerators: Many threads from multiple applications
  Mobile: Interactive + non-interactive consolidation
Different applications with different requirements (SLAs)
  Some applications/threads require performance guarantees
  Modern hierarchies do not distinguish between applications
Applications are increasingly data intensive
  More demand for memory capacity and bandwidth

## Slide 7: Architecture/System Trends
Sharing of memory hierarchy
More cores and components
  More pressure on the memory hierarchy
Asymmetric cores: Performance asymmetry, CPU+GPUs, accelerators, …
  Motivated by energy efficiency and Amdahl’s Law
Different cores have different performance requirements
  Memory hierarchies do not distinguish between cores
Different goals for different systems/users
  System throughput, fairness, per-application performance
  Modern hierarchies are not flexible/configurable

## Slide 8: Summary: Major Trends Affecting Memory
Need for main memory capacity and bandwidth increasing
New need for handling inter-application interference; providing fairness, QoS
Need for memory system flexibility increasing
Main memory energy/power is a key system design concern
DRAM is not scaling well

## Slide 9: Agenda
Technology, Application, Architecture Trends
Requirements from the Memory Hierarchy
Research Challenges and Solution Directions
  Main Memory Scalability
  QoS support: Inter-thread/application interference
Summary

## Slide 10: Requirements from an Ideal Memory System
Traditional
  High system performance
  Enough capacity
  Low cost
New
  Technology scalability
  QoS support and configurability
  Energy (and power, bandwidth) efficiency

## Slide 11: Requirements from an Ideal Memory System
Traditional
  High system performance: Need to reduce inter-thread interference
  Enough capacity: Emerging tech. and waste management can help
  Low cost: Other memory technologies can help
New
  Technology scalability
    Emerging memory technologies (e.g., PCM) can help
  QoS support and configurability
    Need HW mechanisms to control interference and build QoS policies
  Energy (and power, bandwidth) efficiency
    One-size-fits-all design wastes energy; emerging tech. can help?

## Slide 12: Agenda
Technology, Application, Architecture Trends
Requirements from the Memory Hierarchy
Research Challenges and Solution Directions
  Main Memory Scalability
  QoS support: Inter-thread/application interference
Summary

## Slide 13: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 14: Concerns with DRAM as Main Memory
Need for main memory capacity and bandwidth increasing
  DRAM capacity hard to scale
Main memory energy/power is a key system design concern
  DRAM consumes high power due to leakage and refresh
DRAM technology scaling is becoming difficult
  DRAM capacity and cost may not continue to scale

## Slide 15: Possible Solution 1: Tolerate DRAM
Overcome DRAM shortcomings with
  System-level solutions
  Changes to DRAM microarchitecture, interface, and functions

## Slide 16: Possible Solution 2: Emerging Technologies
Some emerging resistive memory technologies are more scalable than DRAM (and they are non-volatile)
Example: Phase Change Memory
  Data stored by changing phase of special material
  Data read by detecting material’s resistance
  Expected to scale to 9nm (2022 [ITRS])
  Prototyped at 20nm (Raoux+, IBM JRD 2008)
  Expected to be denser than DRAM: can store multiple bits/cell
But, emerging technologies have shortcomings as well
  Can they be enabled to replace/augment/surpass DRAM?

## Slide 17: Phase Change Memory: Pros and Cons
Pros over DRAM
  Better technology scaling (capacity and cost)
  Non volatility
  Low idle power (no refresh)
Cons
  Higher latencies: ~4-15x DRAM (especially write)
  Higher active energy: ~2-50x DRAM (especially write)
  Lower endurance (a cell dies after ~108 writes)
Challenges in enabling PCM as DRAM replacement/helper:
  Mitigate PCM shortcomings
  Find the right way to place PCM in the system
  Ensure secure and fault-tolerant PCM operation

## Slide 18: PCM-based Main Memory (I)
How should PCM-based (main) memory be organized?
Hybrid PCM+DRAM [Qureshi+ ISCA’09, Dhiman+ DAC’09]:
  How to partition/migrate data between PCM and DRAM
    Energy, performance, endurance
  Is DRAM a cache for PCM or part of main memory?
  How to design the hardware and software
    Exploit advantages, minimize disadvantages of each technology

## Slide 19: PCM-based Main Memory (II)
How should PCM-based (main) memory be organized?
Pure PCM main memory [Lee et al., ISCA’09, Top Picks’10]:
  How to redesign entire hierarchy (and cores) to overcome PCM shortcomings
    Energy, performance, endurance

## Slide 20: PCM-Based Memory Systems: Research Challenges
Partitioning
  Should DRAM be a cache or main memory, or configurable?
  What fraction? How many controllers?
Data allocation/movement (energy, performance, lifetime)
  Who manages allocation/movement?
  What are good control algorithms?
    Latency-critical, heavily modified  DRAM, otherwise PCM?
    Preventing denial/degradation of service
Design of cache hierarchy, memory controllers, OS
  Mitigate PCM shortcomings, exploit PCM advantages
Design of PCM/DRAM chips and modules
  Rethink the design of PCM/DRAM with new requirements

## Slide 21: An Initial Study: Replace DRAM with PCM
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.
  Surveyed prototypes from 2003-2008 (e.g. IEDM, VLSI, ISSCC)
  Derived “average” PCM parameters for F=90nm

## Slide 22: Results: Naïve Replacement of DRAM with PCM
Replace DRAM with PCM in a 4-core, 4MB L2 system
PCM organized the same as DRAM: row buffers, banks, peripherals
1.6x delay, 2.2x energy, 500-hour average lifetime
Lee, Ipek, Mutlu, Burger, “Architecting Phase Change Memory as a Scalable DRAM Alternative,” ISCA 2009.

## Slide 23: Architecting PCM to Mitigate Shortcomings
Idea 1: Use narrow row buffers in each PCM chip
   Reduces write energy, peripheral circuitry
Idea 2: Use multiple row buffers in each PCM chip
     Reduces array reads/writes  better endurance, latency, energy
Idea 3: Write into array at
cache block or word
granularity
 Reduces unnecessary wear
DRAM
PCM

## Slide 24: Results: Architected PCM as Main Memory
1.2x delay, 1.0x energy, 5.6-year average lifetime
Scaling improves energy, endurance, density
Caveat 1: Worst-case lifetime is much shorter (no guarantees)
Caveat 2: Intensive applications see large performance and energy hits
Caveat 3: Optimistic PCM parameters?

## Slide 25: PCM as Main Memory: Research Challenges
Many research opportunities from technology layer to algorithms layer
Enabling PCM/NVM
  How to maximize performance?
  How to maximize lifetime?
  How to prevent denial of service?
Exploiting PCM/NVM
  How to exploit non-volatility?
  How to minimize energy consumption?
  How to minimize cost?
  How to exploit NVM on chip?
Microarchitecture
ISA
Programs
Algorithms
Problems
Logic
Devices
Runtime System
(VM, OS, MM)
User

## Slide 26: Agenda
Technology, Application, Architecture Trends
Requirements from the Memory Hierarchy
Research Challenges and Solution Directions
  Main Memory Scalability
  QoS support: Inter-thread/application interference
Summary

## Slide 27: Memory System is the Major Shared Resource
threads’ requests
interfere

## Slide 28: Inter-Thread/Application Interference
Problem: Threads share the memory system, but memory system does not distinguish between threads’ requests
Existing memory systems
  Free-for-all, shared based on demand
  Control algorithms thread-unaware and thread-unfair
  Aggressive threads can deny service to others
  Do not try to reduce or control inter-thread interference

## Slide 29: Uncontrolled Interference: An Example
CORE 1
CORE 2
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
DRAM
Bank 0
DRAM
Bank 1
DRAM
Bank 2
Shared DRAM
Memory System
Multi-Core
Chip
unfairness
INTERCONNECT
stream
random
DRAM
Bank 3

## Slide 30: A Memory Performance Hog
// initialize large arrays A, B
for (j=0; j<N; j++) {
index = rand();
A[index] = B[index];
…
}
STREAM
Sequential memory access
Very high row buffer locality (96% hit rate)
Memory intensive
RANDOM
Random memory access
Very low row buffer locality (3% hit rate)
Similarly memory intensive
// initialize large arrays A, B
for (j=0; j<N; j++) {
index = j*linesize;
A[index] = B[index];
…
}
streaming
random
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.

## Slide 31: What Does the Memory Hog Do?
Row Buffer
Row decoder
Column mux
Data
Row 0
T0: Row 0
Row 0
T1: Row 16
T0: Row 0
T1: Row 111
T0: Row 0
T0: Row 0
T1: Row 5
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
T0: Row 0
Memory Request Buffer
T0: STREAM
T1: RANDOM
Row size: 8KB, cache block size: 64B
128 (8KB/64B) requests of T0 serviced before T1
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.

## Slide 32: Effect of the Memory Performance Hog
Chart: 
| STREAM | RANDOM
Column1 | 1.18 | 2.82
1.18X slowdown
2.82X slowdown
Results on Intel Pentium D running Windows XP
(Similar results for Intel Core Duo and AMD Turion, and on Fedora Linux)
Slowdown
Chart: 
| STREAM | gcc
Column1 | 1.23 | 2.91
Chart: 
| STREAM | Virtual PC
Column1 | 1.21 | 2.59
Moscibroda and Mutlu, “Memory Performance Attacks,” USENIX Security 2007.

## Slide 33: Problems due to Uncontrolled Interference
Unfair slowdown of different threads [MICRO’07, ISCA’08, ASPLOS’10]
Low system performance [MICRO’07, ISCA’08, HPCA’10, MICRO’10]
Vulnerability to denial of service [USENIX Security’07]
Priority inversion: unable to enforce priorities/SLAs [MICRO’07]
Poor performance predictability (no performance isolation)
Cores make
very slow
progress
Memory performance hog
Low priority
High priority
Slowdown
Main memory is the only shared resource

## Slide 34: Problems due to Uncontrolled Interference
Unfair slowdown of different threads [MICRO’07, ISCA’08, ASPLOS’10]
Low system performance [MICRO’07, ISCA’08, HPCA’10, MICRO’10]
Vulnerability to denial of service [USENIX Security’07]
Priority inversion: unable to enforce priorities/SLAs [MICRO’07]
Poor performance predictability (no performance isolation)

## Slide 35: How Do We Solve The Problem?
Inter-thread interference is uncontrolled in all memory resources
  Memory controller
  Interconnect
  Caches
We need to control it
  i.e., design an interference-aware (QoS-aware) memory system

## Slide 36: QoS-Aware Memory Systems: Challenges
How do we reduce inter-thread interference?
  Improve system performance and core utilization
  Reduce request serialization and core starvation
How do we control inter-thread interference?
  Provide mechanisms to enable system software to enforce QoS policies
  While providing high system performance
How do we make the memory system configurable/flexible?
  Enable flexible mechanisms that can achieve many goals
    Provide fairness or throughput when needed
    Satisfy performance guarantees when needed

## Slide 37: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ CMU TR’11]
  QoS-aware thread scheduling to cores

## Slide 38: Agenda
Technology, Application, Architecture Trends
Requirements from the Memory Hierarchy
Research Challenges and Solution Directions
  Main Memory Scalability
  QoS support: Inter-thread/application interference
    Smart Resources: Thread Cluster Memory Scheduling
    Dumb Resources: Fairness via Source Throttling
Summary

## Slide 39: QoS-Aware Memory Scheduling
How to schedule requests to provide
  High system performance
  High fairness to applications
  Configurability to system software
Memory controller needs to be aware of threads
Memory Controller
Core
Core
Core
Core
Memory
Resolves memory contention by scheduling requests

## Slide 40: QoS-Aware Memory Scheduling: Evolution
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
  Idea: Estimate and balance thread slowdowns
  Takeaway: Proportional thread progress improves performance, especially when threads are “heavy” (memory intensive)
Parallelism-aware batch scheduling [Mutlu+ ISCA’08, Top Picks’09]
  Idea: Rank threads and service in rank order (to preserve bank parallelism); batch requests to prevent starvation
ATLAS memory scheduler [Kim+ HPCA’10]

## Slide 41: Within-Thread Bank Parallelism
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread A
thread B
thread execution timeline
WAIT
WAIT
thread B
thread A
Bank 0
Bank 1
req
req
req
req
memory service timeline
thread execution timeline
WAIT
WAIT
rank
thread B
thread A
thread A
thread B
SAVED CYCLES
Key Idea:
Notes: A memory scheduler can actively exploit bank-level parallelism to reduce the effective memory access latency. Here’s how.
Let us assume a case where two threads send two memory requests to two different banks.
A naïve memory scheduler that doesn’t exploit bank-level parallelism would schedule the requests in the order they arrived.
As shown in their thread execution timeline, both threads must wait for two bank latencies before all their requests are serviced.
In contrast, a memory scheduler that is aware of bank-level parallelism was proposed by Mutlu and Moscibroda.
Their key idea was to rank the threads so that thread’s memory requests are prioritized in the same order across all the banks.
In this case, let us assume that the blue thread’s request are the most prioritized.
The scheduler would then reorder the requests at bank 1’s request buffer…
so that the blue requests are serviced concurrently, after which the red requests can be serviced concurrently.
The memory service timeline shows how the access latencies for requests from the same thread are overlapped.
And, as a result, thread A has to wait less for its requests to be serviced.

## Slide 42: QoS-Aware Memory Scheduling: Evolution
Stall-time fair memory scheduling [Mutlu+ MICRO’07]
  Idea: Estimate and balance thread slowdowns
  Takeaway: Proportional thread progress improves performance, especially when threads are “heavy” (memory intensive)
Parallelism-aware batch scheduling [Mutlu+ ISCA’08, Top Picks’09]
  Idea: Rank threads and service in rank order (to preserve bank parallelism); batch requests to prevent starvation
  Takeaway: Preserving within-thread bank-parallelism improves performance; request batching improves fairness
ATLAS memory scheduler [Kim+ HPCA’10]
  Idea: Prioritize threads that have attained the least service from the memory scheduler
  Takeaway: Prioritizing “light” threads improves performance

## Slide 43: Previous Scheduling Algorithms are Biased
No previous memory scheduling algorithm provides both the best fairness and system throughput
Chart: Weighted Speedup
| 7.21 | 8.166 | 8.26 | 8.527000000000001 | 8.777999999999998
FCFS | 8.513
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
System throughput bias
Fairness bias
Ideal
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads

## Slide 44: Throughput vs. Fairness
  Take turns accessing memory
Fairness biased approach
thread C
thread B
thread A
less memory intensive
higher
priority
  Prioritize less memory-intensive threads
Throughput biased approach
  Good for throughput
starvation  unfairness
thread C
thread B
thread A
  Does not starve
not prioritized 
reduced throughput
Single policy for all threads is insufficient

## Slide 45: Achieving the Best of Both Worlds
thread
thread
higher
priority
thread
thread
thread
thread
thread
thread
  Prioritize memory-non-intensive threads
For Throughput
  Unfairness caused by memory-intensive being prioritized over each other
    Shuffle thread ranking
  Memory-intensive threads have different vulnerability to interference
    Shuffle asymmetrically
For Fairness
thread
thread
thread
thread

## Slide 46: Thread Cluster Memory Scheduling [Kim+ MICRO’10]
Group threads into two clusters
Prioritize non-intensive cluster
Different policies for each cluster
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness

## Slide 47: TCM: Throughput and Fairness
Chart: Weighted Speedup
| 8.166 | 8.26 | 8.527000000000001 | 8.777999999999998 | 9.179
FRFCFS | 14.18
STFM | 9.245
PAR-BS | 7.418
ATLAS | 11.52
TCM | 7.074
Better system throughput
Better fairness
24 cores, 4 memory controllers, 96 workloads
TCM, a heterogeneous scheduling policy,
provides best fairness and system throughput

## Slide 48: TCM: Fairness-Throughput Tradeoff
Chart: Weighted Speedup
| 12.73 | 13.0 | 13.03 | 13.04 | 12.97 | 12.81 | 12.66 | 12.48 | 13.11 | 13.21 | 13.21 | 13.19 | 13.16 | 13.06 | 13.6 | 13.76 | 13.61 | 13.68 | 13.65 | 13.62 | 14.49 | 14.58 | 14.8 | 14.84 | 14.83 | 14.43 | 14.04 | 14.4 | 14.63 | 14.79 | 14.92
FRFCFS | 9.825 | 6.73 | 5.84 | 5.38 | 5 | 5.07 | 5.5 | 5.73
STFM | 5.949 | 6.215 | 6.423 | 6.923 | 6.953 | 7.263
PAR-BS | 5.999 | 5.449 | 5.423 | 5.075 | 4.905 | 4.82
ATLAS | 7.018 | 7.139 | 7.422 | 7.501 | 7.552 | 7.458
TCM | 4.843 | 4.952 | 5.258 | 5.503 | 5.727
When configuration parameter is varied…
Adjusting ClusterThreshold
TCM allows robust fairness-throughput tradeoff
STFM
PAR-BS
ATLAS
TCM
Better system throughput
Better fairness
FRFCFS

## Slide 49: Agenda
Technology, Application, Architecture Trends
Requirements from the Memory Hierarchy
Research Challenges and Solution Directions
  Main Memory Scalability
  QoS support: Inter-thread/application interference
    Smart Resources: Thread Cluster Memory Scheduling
    Dumb Resources: Fairness via Source Throttling
Summary

## Slide 50: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ CMU TR’11]
  QoS-aware thread scheduling to cores

## Slide 51: Many Shared Resources
Core 0
Core 1
Core 2
Core N
Shared Cache
Memory Controller
DRAM
Bank 0
DRAM
Bank 1
DRAM Bank 2
...
DRAM Bank K
...
Shared Memory
Resources
Chip Boundary
On-chip
Off-chip
51

## Slide 52: The Problem with “Smart Resources”
Independent interference control mechanisms in caches, interconnect, and memory can contradict each other
Explicitly coordinating mechanisms for different resources requires complex implementation
How do we enable fair sharing of the entire memory system by controlling interference in a coordinated manner?

## Slide 53: An Alternative Approach: Source Throttling
Manage inter-thread interference at the cores, not at the shared resources
Dynamically estimate unfairness in the memory system
Feed back this information into a controller
Throttle cores’ memory access rates accordingly
  Whom to throttle and by how much depends on performance target (throughput, fairness, per-thread QoS, etc)
  E.g., if unfairness > system-software-specified target then throttle down core causing unfairness & throttle up core that was unfairly treated
Ebrahimi et al., “Fairness via Source Throttling,” ASPLOS’10.

## Slide 54: Fairness via Source Throttling (FST) [ASPLOS’10]
54
Runtime Unfairness
Evaluation
Dynamic
Request Throttling
1- Estimating system unfairness
2- Find app. with the highest slowdown (App-slowest)
3- Find app. causing most interference for App-slowest (App-interfering)
if (Unfairness Estimate >Target)
{
1-Throttle down App-interfering
(limit injection rate and parallelism)
2-Throttle up App-slowest
}
FST
Unfairness Estimate
App-slowest
App-interfering
⎪
⎨
⎪
⎧
⎩
Slowdown Estimation
Time
Interval 1
Interval 2
Interval 3
Runtime Unfairness
Evaluation
Dynamic
Request Throttling

## Slide 55: System Software Support
Different fairness objectives can be configured by system software
  Keep maximum slowdown in check
    Estimated Max Slowdown < Target Max Slowdown
  Keep slowdown of particular applications in check to achieve a particular performance target
    Estimated Slowdown(i) < Target Slowdown(i)
Support for thread priorities
  Weighted Slowdown(i) = Estimated Slowdown(i) x Weight(i)

## Slide 56: Source Throttling Results: Takeaways
Source throttling alone provides better performance than a combination of “smart” memory scheduling and fair caching
  Decisions made at the memory scheduler and the cache sometimes contradict each other
Neither source throttling alone nor “smart resources” alone provides the best performance
Combined approaches are even more powerful
  Source throttling and resource-based interference control

## Slide 57: Designing QoS-Aware Memory Systems: Approaches
Smart resources: Design each shared resource to have a configurable interference control/reduction mechanism
  QoS-aware memory controllers [Mutlu+ MICRO’07] [Moscibroda+, Usenix Security’07] [Mutlu+ ISCA’08, Top Picks’09] [Kim+ HPCA’10] [Kim+ MICRO’10, Top Picks’11]
  QoS-aware interconnects [Das+ MICRO’09, ISCA’10, Top Picks ’11] [Grot+ MICRO’09, ISCA’11]
  QoS-aware caches
Dumb resources: Keep each resource free-for-all, but reduce/control interference by injection control or data mapping
  Source throttling to control access to memory system [Ebrahimi+ ASPLOS’10, ISCA’11] [Ebrahimi+ MICRO’09] [Nychis+ HotNets’10]
  QoS-aware data mapping to memory controllers [Muralidhara+ CMU TR’11]
  QoS-aware thread scheduling to cores

## Slide 58: Another Way of Reducing Interference
Memory Channel Partitioning
  Idea: Map badly-interfering applications’ pages to different channels [Muralidhara+ CMU TR’11]
Separate data of low/high intensity and low/high row-locality applications
Especially effective in reducing interference of threads with “medium” and “heavy” memory intensity

## Slide 59: Summary: Memory QoS Approaches and Techniques
Approaches: Smart vs. dumb resources
  Smart resources: QoS-aware memory scheduling
  Dumb resources: Source throttling; channel partitioning
  Both approaches are effective in reducing interference
  No single best approach for all workloads
Techniques: Request scheduling, source throttling, memory partitioning
  All approaches are effective in reducing interference
  Can be applied at different levels: hardware vs. software
  No single best technique for all workloads
Combined approaches and techniques are the most powerful
  Integrated Memory Channel Partitioning and Scheduling

## Slide 60: Two Related Talks at ISCA
How to design QoS-aware memory systems (memory scheduling and source throttling) in the presence of prefetching
  Ebrahimi et al., “Prefetch-Aware Shared Resource Management for Multi-Core Systems,” ISCA’11.
  Monday afternoon (Session 3B)
How to design scalable QoS mechanisms in on-chip interconnects
  Idea: Isolate shared resources in a region, provide QoS support only within the region, ensure interference-free access to the region
  Grot et al., “Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees,” ISCA’11.
  Wednesday morning (Session 8B)

## Slide 61: Agenda
Technology, Application, Architecture Trends
Requirements from the Memory Hierarchy
Research Challenges and Solution Directions
  Main Memory Scalability
  QoS support: Inter-thread/application interference
    Smart Resources: Thread Cluster Memory Scheduling
    Dumb Resources: Fairness via Source Throttling
Conclusions

## Slide 62: Conclusions
Technology, application, architecture trends dictate new needs from memory system
A fresh look at (re-designing) the memory hierarchy
  Scalability: Enabling new memory technologies
  QoS, fairness & performance: Reducing and controlling inter-application interference: QoS-aware memory system design
  Efficiency: Customizability, minimal waste, new technologies
Many exciting research topics in fundamental areas across the system stack
  Hardware/software/device cooperation essential

## Slide 63: Thank you.

## Slide 64: Memory Systems in the Many-Core Era: Some Challenges and Solution Directions
Onur Mutlu
onur@cmu.edu
June 5, 2011
ISMM/MSPC