## Slide 1
Enabling Massively Parallel Computation in DRAM via Lookup Tables
João Dinis Ferreira |  | Gabriel Falcao |  | Juan Gómez-Luna |  | Mohammed Alser
Lois Orosa |  | Mohammad Sadrosadati |  | Jeremie S. Kim |  | Geraldo F. Oliveira
Taha Shahroodi |  | Anant Nori |  | Onur Mutlu
pLUTo
Notes: GOOD AFTERNOON
MY NAME IS JOÃO DINIS FERREIRA AND I AM THRILLED TO INTRODUCE OUR WORK PLUTO: ENABLING MASSIVELY PARALLEL COMPUTATION IN DRAM VIA LOOKUP TABLES

## Slide 2
Background: Processing-in-Memory (PiM) alleviates the performance and energy bottlenecks caused by data movement in modern applications
  Processing-near-Memory (PnM): adds logic elements near memory arrays
  Processing-using-Memory (PuM): uses the analog properties of memory for computation
Problem: Existing Processing-using-DRAM architectures only support a limited range of operations (data movement, bitwise logic, bit shifting)
  This limits Processing-using-DRAM’s applicability to a narrow set of applications
Goal: Extend the applicability of Processing-using-DRAM by designing a PuM substrate with support for complex operations
pLUTo: A Processing-using-DRAM substrate that replaces complex operations with equivalent memory lookups
  pLUTo LUT Query operation enables bulk in-memory table lookups
  Three pLUTo designs target different performance/energy/area tradeoffs
  pLUTo API and pLUTo Compiler facilitate programmer adoption
Key Results: Our extensive evaluation shows that pLUTo
  Greatly outperforms CPU/GPU/PnM baselines, both in performance and energy
  Incurs small DRAM area overheads (between 10.2% and 23.1%)
Summary
  https://github.com/CMU-SAFARI/pLUTo
Notes: A GROWING NUMBER OF PROCESSING-IN-MEMORY ARCHITECTURES HAVE BEEN PROPOSED IN RECENT YEARS TO ADDRESS THE GROWING DATA MOVEMENT BOTTLENECK THAT AFFECTS MANY MODERN APPLICATIONS.
TWO IMPORTANT CLASSES OF PIM EXIST: PNM, WHICH <READ SLIDE>, AND PUM, WHICH <READ SLIDE>.
WHILE PUM ADOPTED BY MULTIPLE MEMORY TECHNOLOGIES, IN THIS TALK I WILL FOCUS ON PROCESSING-USING-DRAM.
WHILE EXISTING PUD ARCHITECTURES PROVIDE VERY HIGH THROUGHPUT AND EFFICIENCY, THEY ONLY SUPPORT A LIMITED RANGE OF OPERATIONS, WHICH LIMITS THEIR APPLICABILITY TO A NARROW DOMAIN.
BASED ON THIS OBSERVATION, WE IDENTIFIED THE GOAL OF EXTENDING THE APPLICABILITY… <READ SLIDE>
TO THIS END, WE DESCRIBE PLUTO, A <READ SLIDE>
THE PLUTO LUT QUERY IS AT THE CORE OF PLUTO: THIS IS THE OPERATION THAT ENABLES… <READ SLIDE>
<READ SLIDE>
<READ SLIDE>
OUR EVALUATION SHOWS THAT PLUTO ACHIEVES BETWEEN 1 AND 3 ORDERS OF MAGNITUDE SPEEDUP RELATIVE TO THE BASELINE SYSTEMS, WHILE INCURRING… <READ SLIDE>
DON’T SAY AREA, SAY WE HAVE GITHUB.

## Slide 3
Introduction
Evaluation
Conclusion
Contents
pLUTo
System Integration
pLUTo Designs
Overview
Notes: THIS IS THE OUTLINE OF MY TALK

## Slide 4
Introduction
Evaluation
Conclusion
Contents
pLUTo
System Integration
pLUTo Designs
Overview
Notes: I WILL BEGIN BY CLEARLY DESCRIBING OUR PROBLEM STATEMENT.

## Slide 5
Data Movement Bottleneck
Memory
Channel
Main Memory
Computing Unit
(CPU, GPU, FPGA, Accelerators)
Data movement is a major bottleneck in modern computer architectures
Notes: THE DATA MOVEMENT IS A MAJOR BOTTLENECK IN MODERN COMPUTER ARCHITECTURES

## Slide 6
Data Movement Bottleneck
Memory
Channel
power-hungry
bandwidth-limited
Main Memory
Computing Unit
(CPU, GPU, FPGA, Accelerators)
Data movement is a major bottleneck in modern computer architectures
Notes: THIS IS DUE TO THE BANDWIDTH-LIMITED AND POWER-HUNGRY NATURE OF THE MEMORY CHANNEL THAT CONNECTS MAIN MEMORY TO THE COMPUTING UNITS OF CONVENTIONAL SYSTEMS

## Slide 7
Data Movement Bottleneck
Memory
Channel
power-hungry
bandwidth-limited
Main Memory
Computing Unit
(CPU, GPU, FPGA, Accelerators)
Data movement is a major bottleneck in modern computer architectures
Over 60% of the total system energy is spent on data movement1
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018
Notes: IN FACT, A RECENT PROFILING EFFORT HAS SHOWN THAT THE MAJORITY OF THE SYSTEM’S ENERGY IS TAKEN UP BY DATA MOVEMENT

## Slide 8
Processing-in-Memory
Computing Unit
(CPU, GPU, FPGA, Accelerators)
Memory
Channel
Main Memory
Processing-near-Memory leverages additional logic placed on the same die as memory or on the logic layer of 3D-stacked memory
1. Processing-near-Memory
Notes: TO ADDRESS THIS NARROWING BOTTLENECK BETWEEN COMPUTING UNITS AND MEMORY UNITS, RECENT RESEARCH EFFORTS HAVE PROPOSED VARIOUS MECHANISMS TO PERFORM PROCESSING-IN-MEMORY.
THAT IS, TO INTRODUCE SOME FORM OF COMPUTE CAPABILITY IN THE MAIN MEMORY.
<CLICK>
ONE SUBSET OF PROCESSING-IN-MEMORY IS PROCESSING-NEAR-MEMORY: UNDER THIS PARADIGM, ADDITIONAL LOGIC IS ADDED EITHER TO THE MEMORY DIE OR TO THE LOGIC LAYER OF 3D-STACKED MEMORIES.

## Slide 9
Computing Unit
(CPU, GPU, FPGA, Accelerators)
Main Memory
Processing-using-Memory leverages the operational principles of memory to perform computation
2. Processing-using-Memory
Memory
Channel
Processing-in-Memory
Notes: IN CONTRAST, A DIFFERENT BODY OF WORK EXPLORES THE NOTION OF <CLICK> PROCESSING-**USING**-MEMORY, THAT IS, <CLICK> TO LEVERAGE THE ANALOG OPERATIONAL PRINCIPLES OF MEMORY DEVICES TO PERFORM VARIOUS KINDS OF COMPUTATION <POINT> **INSIDE** THE MEMORY ARRAY ITSELF.
WHILE THIS APPROACH OFTEN PROVIDES THE HIGHEST THROUGHPUT AND ENERGY EFFICIENCY, THE RANGE OF OPERATIONS THAT THESE ARCHITECTURES SUPPORT IS VERY LIMITED.

## Slide 10: Limitations of Processing-using-DRAM
Data Movement | RowClone, Seshadri+ 2013 LISA, Chang+ 2013
Bitwise Operations | Ambit, Seshadri+ 2017
Bit Shifting | DRISA, Li+ 2017
Arithmetic Operations | SIMDRAM, Hajinazar & Oliveira+ 2021
Existing Processing-using-DRAM architectures only support a limited range of operations
Notes: THE RANGE OF OPERATIONS SUPPORTED BY PRIOR PROCESSING-USING-MEMORY PROPOSALS IS LIMITED TO DATA MOVEMENT, BITWISE OPERATIONS, BUT SHIFTING, AND ARITHMETIC OPERATIONS.
THIS LIMITS THE POTENTIAL OF PROCESSING-USING-MEMORY TO TARGET MANY REAL-WORLD APPLICATIONS THAT REQUIRE MORE COMPLEX OPERATIONS.

## Slide 11: The Goal of pLUTo
Extend Processing-using-DRAM to support the execution of arbitrarily complex operations
Notes: STATED PLAINLY, THE GOAL OF PLUTO IS THUS, PRECISELY, TO **EXTEND**…

## Slide 12
Introduction
Evaluation
Conclusion
Contents
pLUTo
System Integration
pLUTo Designs
Overview
Notes: LET’S NOW UNDERSTAND THE OPERATION OF pLUTo.

## Slide 13
pLUTo: Key Idea
?
output
x
input
x
x
ALU
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 14
f(x)
x
pLUTo: Key Idea
?
output
x
input
x
ALU
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 15
x
pLUTo: Key Idea
?
output
x
input
x
ALU
f(x)
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 16
input
output
x
x
pLUTo: Key Idea
ALU
x
input
f(x)
output
x
?
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 17
x
input
?
output
x
pLUTo: Key Idea
ALU
x
input
f(x)
output
x
x
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 18
?
input
output
x
pLUTo: Key Idea
ALU
x
input
f(x)
output
x
x
LUT[x]
x
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 19
input
LUT[x]
output
x
x
ALU
x
input
f(x)
output
x
pLUTo: Key Idea
Replace computation with memory accesses
→ pLUTo LUT Query operation
Notes: TO DO SO, LET’S BEGIN BY CONSIDERING THE KEY IDEA BEHIND PLUTO’S OPERATION.
CONVENTIONAL ARCHITECTURES EMPLOY DEDICATED ARITHMETIC LOGIC UNITS, ALUS <POINT>, TO
HIGH-LEVEL KEY IDEA: INTRODUCE THE CONCEPT OF LUT QUERY
  WHAT DOES IT PROVIDE AND HOW IT FIXES THE PROBLEM WE STATED BEFORE?

## Slide 20
The pLUTo LUT Query: Setup
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
{2nd, 1st, 2nd, 4th}
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 21
The pLUTo LUT Query: Setup
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
input vector
{2nd, 1st, 2nd, 4th}
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 22
The pLUTo LUT Query: Setup
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
input vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
LUT index
0
1
2
3
lookup table
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 23
The pLUTo LUT Query: Setup
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
input vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
LUT index
0
1
2
3
1 |  |  | 
lookup table
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 24
The pLUTo LUT Query: Setup
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
input vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
LUT index
0
1
2
3
1 | 0 |  | 
lookup table
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 25
The pLUTo LUT Query: Setup
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
input vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
LUT index
0
1
2
3
1 | 0 | 1 | 
lookup table
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 26
The pLUTo LUT Query: Setup
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
input vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
LUT index
0
1
2
3
1 | 0 | 1 | 3
lookup table
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 27
The pLUTo LUT Query: Setup
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
LUT index
0
1
2
3
1 | 0 | 1 | 3
lookup table
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 28
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
LUT index
0
1
2
3
lookup table
The pLUTo LUT Query: Setup
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 29
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
LUT index
0
1
2
3
in-memory
lookup table
lookup table
The pLUTo LUT Query: Setup
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 30
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
3
3
LUT index
0
1
2
3
in-memory
lookup table
1st
2nd
3rd
4th
The pLUTo LUT Query: Setup
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 31
The pLUTo LUT Query: Operation
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
3
3
LUT index
0
1
2
3
in-memory
lookup table
1st
2nd
3rd
4th
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 32
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
3
The pLUTo LUT Query: Operation
in-memory
lookup table
LUT index
0
1
2
3
1st
2nd
3rd
4th
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 33
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
3 |  |  | 
2
2
The pLUTo LUT Query: Operation
in-memory
lookup table
LUT index
0
1
2
3
1st
2nd
3rd
4th
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 34
3 |  |  | 
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
2
The pLUTo LUT Query: Operation
in-memory
lookup table
LUT index
0
1
2
3
1st
2nd
3rd
4th
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 35
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
3
3 | 2 |  | 
3
The pLUTo LUT Query: Operation
in-memory
lookup table
LUT index
0
1
2
3
1st
2nd
3rd
4th
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 36
3 | 2 |  | 
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
3
3
The pLUTo LUT Query: Operation
in-memory
lookup table
LUT index
0
1
2
3
1st
2nd
3rd
4th
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 37
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
3 | 2 | 3 | 
7
7
The pLUTo LUT Query: Operation
in-memory
lookup table
LUT index
0
1
2
3
1st
2nd
3rd
4th
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 38
3 | 2 | 3 | 
Return {2nd, 1st, 2nd, 4th} prime numbers
Desired LUT Query
1 | 0 | 1 | 3
input vector
output vector
{2nd, 1st, 2nd, 4th}
Prime numbers | A
i | f(i)
1st | 2
2nd | 3
3rd | 5
4th | 7
7
7
The pLUTo LUT Query: Operation
in-memory
lookup table
LUT index
0
1
2
3
1st
2nd
3rd
4th
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 39
row buffer
In-DRAM pLUTo LUT Query: Setup
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
0
1
2
3
row decoder
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 40
In-DRAM pLUTo LUT Query: Setup
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
0
1
2
3
row buffer
row decoder
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 41
row buffer
row decoder
0
1
2
3
In-DRAM pLUTo LUT Query: Setup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
2
3
5
7
2
3
5
7
2
3
5
7
Multiple copies of the lookup table
→ exploit DRAM parallelism
2
3
5
7
2
3
5
7
DRAM array
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 42
In-DRAM pLUTo LUT Query: Setup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
0
1
2
3
pLUTo
row sweep
DRAM array
row buffer
2
3
5
7
2
3
5
7
2
3
5
7
2
3
5
7
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 43
0
0
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 44
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
row buffer
match logic
Accessing
the 2nd (1) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 45
match logic
Accessing
the 2nd (1) prime number?
input
vector
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
input
vector
row buffer
pLUTo
row sweep
0 = 1 ?
1
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 46
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
?
𝘅
input
vector
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 47
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
?
𝘅
input
vector
input
vector
row buffer
Accessing
the 1st (0) prime number?
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 48
input
vector
Accessing
the 1st (0) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
output
vector
DRAM array
1
2
3
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
row buffer
𝘅
0
pLUTo
row sweep
0 = 0 ?
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 49
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 50
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 1st (0) prime number?
input
vector
?
✓
input
vector
2
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 51
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
Accessing
the 2nd (1) prime number?
input
vector
?
✓
𝘅
input
vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 52
Accessing
the 4th (3) prime number?
In-DRAM pLUTo LUT Query: Step 1
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
𝘅
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
DRAM array
0
1
2
3
pLUTo
row sweep
2 | 2 | 2 | 2
2 | 2 | 2 | 2
match logic
input
vector
?
✓
𝘅
𝘅
input
vector
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 53
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
3 | 3 | 3 | 3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 54
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
✓
𝘅
✓
𝘅
3 | 3 | 3 | 3
3
3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 55
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | 2 | - | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
✓
𝘅
✓
𝘅
3 | 3 | 3 | 3
3
3
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 56
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
1
2
3
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 57
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
1
2
3
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 58
output
vector
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 3
1 | 0 | 1 | 3
3 | 2 | 3 | -
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
0
3
𝘅
𝘅
1
2
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
𝘅
𝘅
5 | 5 | 5 | 5
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 59
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
0
1
2
3
7 | 7 | 7 | 7
3 | 2 | 3 | -
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 60
0
1
2
3
output
vector
3 | 2 | 3 | -
- | - | - | -
7 | 7 | 7 | 7
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
match logic
DRAM array
𝘅
✓
𝘅
7
𝘅
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 61
0
1
2
3
pLUTo
row sweep
In-DRAM pLUTo LUT Query: Step 4
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
?
?
?
?
input vector
 | Prime numbers | A
LUT index | i | f(i)
0 | 1st | 2
1 | 2nd | 3
2 | 3rd | 5
3 | 4th | 7
1 | 0 | 1 | 3
lookup table
output vector
3 | 2 | 3 | 7
LUT Query: Return {2nd, 1st, 2nd, 4th}
prime numbers
input
vector
output
vector
match logic
DRAM array
7 | 7 | 7 | 7
𝘅
✓
𝘅
𝘅
3 | 2 | 3 | -
7
row buffer
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 62
Introduction
Evaluation
Conclusion
Contents
pLUTo
System Integration
pLUTo Designs
Overview

## Slide 63
pLUTo Designs
Match Logic: shared by the three pLUTo designs
BSA
Buffered Sense Amplifier
GMC
Gated Memory Cell
GSA
Gated Sense Amplifier
Notes: WHILE I UNFORTUNATELY DO NOT HAVE TIME TO EXPLAIN THE OPERATION OF EACH OF THE THREE DESIGNS IN DETAIL, I DO WANT TO LEAVE YOU WITH SOME INTUITION AS TO HOW THEY WORK: THE MAIN DIFFERENCE BETWEEN

## Slide 64
pLUTo Designs
Match Logic: shared by the three pLUTo designs
BSA
Buffered Sense Amplifier
GMC
Gated Memory Cell
GSA
Gated Sense Amplifier
Notes: WHILE I UNFORTUNATELY DO NOT HAVE TIME TO EXPLAIN THE OPERATION OF EACH OF THE THREE DESIGNS IN DETAIL, I DO WANT TO LEAVE YOU WITH SOME INTUITION AS TO HOW THEY WORK: THE MAIN DIFFERENCE BETWEEN

## Slide 65
pLUTo Designs
Match Logic: shared by the three pLUTo designs
BSA
Buffered Sense Amplifier
GMC
Gated Memory Cell
GSA
Gated Sense Amplifier
Notes: NOTE THAT THIS PROCESS, WHICH I HAVE SO FAR PRESENTED IN AN IMPLEMENTATION-AGNOSTIC MANNER, REQUIRES TWO IMPORTANT COMPONENTS THAT ARE NOT PRESENT IN COMMODITY DRAM.
FIRST, THE **MATCH LOGIC** THAT IS INDENTIFIES MATCHES BETWEEN THE INDEX OF THE CURRENTLY ACTIVATED ROW AND EACH OF THE ELEMENTS IN THE SOURCE ROW BUFFER.
THIS HARDWARE COMPONENT IS SHARED BY ALL PLUTO DESIGNS AND IS ALWAYS IMPLEMENTED IN THE SAME WAY.
AND WE KNOW THAT THE MATCH LOGIC GIVES US THE ABILITY TO… <EXPLAIN M-C SWITCH>
THERE IS HOWEVER, A LESS TRIVIAL TASK TO ACCOMPLISH: THAT OF STORING INTERMEDIATE RESULTS AS THE RESULT OF THE PLUTO LUT QUERY IS PROGRESSIVELY CONSTRUCTED.
SOLVING THIS CHALLENGE ESSENTIALLY AMOUNTS TO FINDING A WAY OF BUFFERING THESE INTERMEDIATE RESULTS.
WE EXPLORE THREE DIFFERENT WAYS TO DO THIS, WITH DIFFERENT PERFORMANCE, ENERGY EFFICIENCY AND AREA OVERHEAD TRADE-OFFS.

## Slide 66
pLUTo Designs
Match Logic: shared by the three pLUTo designs
BSA
Buffered Sense Amplifier
GMC
Gated Memory Cell
GSA
Gated Sense Amplifier
Notes: NOTE THAT THIS PROCESS, WHICH I HAVE SO FAR PRESENTED IN AN IMPLEMENTATION-AGNOSTIC MANNER, REQUIRES TWO IMPORTANT COMPONENTS THAT ARE NOT PRESENT IN COMMODITY DRAM.
FIRST, THE **MATCH LOGIC** THAT IS INDENTIFIES MATCHES BETWEEN THE INDEX OF THE CURRENTLY ACTIVATED ROW AND EACH OF THE ELEMENTS IN THE SOURCE ROW BUFFER.
THIS HARDWARE COMPONENT IS SHARED BY ALL PLUTO DESIGNS AND IS ALWAYS IMPLEMENTED IN THE SAME WAY.
AND WE KNOW THAT THE MATCH LOGIC GIVES US THE ABILITY TO… <EXPLAIN M-C SWITCH>
THERE IS HOWEVER, A LESS TRIVIAL TASK TO ACCOMPLISH: THAT OF STORING INTERMEDIATE RESULTS AS THE RESULT OF THE PLUTO LUT QUERY IS PROGRESSIVELY CONSTRUCTED.
SOLVING THIS CHALLENGE ESSENTIALLY AMOUNTS TO FINDING A WAY OF BUFFERING THESE INTERMEDIATE RESULTS.
WE EXPLORE THREE DIFFERENT WAYS TO DO THIS, WITH DIFFERENT PERFORMANCE, ENERGY EFFICIENCY AND AREA OVERHEAD TRADE-OFFS.

## Slide 67
pLUTo Designs
Match Logic: shared by the three pLUTo designs
BSA
Buffered Sense Amplifier
GMC
Gated Memory Cell
GSA
Gated Sense Amplifier
Notes: NOTE THAT THIS PROCESS, WHICH I HAVE SO FAR PRESENTED IN AN IMPLEMENTATION-AGNOSTIC MANNER, REQUIRES TWO IMPORTANT COMPONENTS THAT ARE NOT PRESENT IN COMMODITY DRAM.
FIRST, THE **MATCH LOGIC** THAT IS INDENTIFIES MATCHES BETWEEN THE INDEX OF THE CURRENTLY ACTIVATED ROW AND EACH OF THE ELEMENTS IN THE SOURCE ROW BUFFER.
THIS HARDWARE COMPONENT IS SHARED BY ALL PLUTO DESIGNS AND IS ALWAYS IMPLEMENTED IN THE SAME WAY.
AND WE KNOW THAT THE MATCH LOGIC GIVES US THE ABILITY TO… <EXPLAIN M-C SWITCH>
THERE IS HOWEVER, A LESS TRIVIAL TASK TO ACCOMPLISH: THAT OF STORING INTERMEDIATE RESULTS AS THE RESULT OF THE PLUTO LUT QUERY IS PROGRESSIVELY CONSTRUCTED.
SOLVING THIS CHALLENGE ESSENTIALLY AMOUNTS TO FINDING A WAY OF BUFFERING THESE INTERMEDIATE RESULTS.
WE EXPLORE THREE DIFFERENT WAYS TO DO THIS, WITH DIFFERENT PERFORMANCE, ENERGY EFFICIENCY AND AREA OVERHEAD TRADE-OFFS.

## Slide 68
pLUTo Designs
Match Logic: shared by the three pLUTo designs
BSA
Buffered Sense Amplifier
GMC
Gated Memory Cell
GSA
Gated Sense Amplifier
Notes: NOTE THAT THIS PROCESS, WHICH I HAVE SO FAR PRESENTED IN AN IMPLEMENTATION-AGNOSTIC MANNER, REQUIRES TWO IMPORTANT COMPONENTS THAT ARE NOT PRESENT IN COMMODITY DRAM.
FIRST, THE **MATCH LOGIC** THAT IS INDENTIFIES MATCHES BETWEEN THE INDEX OF THE CURRENTLY ACTIVATED ROW AND EACH OF THE ELEMENTS IN THE SOURCE ROW BUFFER.
THIS HARDWARE COMPONENT IS SHARED BY ALL PLUTO DESIGNS AND IS ALWAYS IMPLEMENTED IN THE SAME WAY.
AND WE KNOW THAT THE MATCH LOGIC GIVES US THE ABILITY TO… <EXPLAIN M-C SWITCH>
THERE IS HOWEVER, A LESS TRIVIAL TASK TO ACCOMPLISH: THAT OF STORING INTERMEDIATE RESULTS AS THE RESULT OF THE PLUTO LUT QUERY IS PROGRESSIVELY CONSTRUCTED.
SOLVING THIS CHALLENGE ESSENTIALLY AMOUNTS TO FINDING A WAY OF BUFFERING THESE INTERMEDIATE RESULTS.
WE EXPLORE THREE DIFFERENT WAYS TO DO THIS, WITH DIFFERENT PERFORMANCE, ENERGY EFFICIENCY AND AREA OVERHEAD TRADE-OFFS.

## Slide 69
pLUTo Designs: Tradeoff Space
Chart: 
| Performance | Energy Efficiency | Area Efficiency
BSA | 8 | 8 | 5
GSA | 4 | 4 | 10
GMC | 10 | 10 | 3
v
Performance
Area Efficiency
Energy Efficiency
Gated Sense Amplifier
Buffered Sense Amplifier
Gated Memory Cell
pLUTo designs cover a broad design space and provide different performance, energy, and area efficiency

## Slide 70
Introduction
Evaluation
Conclusion
Contents
pLUTo
System Integration
pLUTo Designs
Overview

## Slide 71
System Integration
C-Like Code with
pLUTo API calls
Assembly Code with pLUTo ISA Extensions
Execution in the DRAM Substrate
pLUTo Compiler
pLUTo Controller
api_pluto_mul
pluto_subarray_alloc
pluto_bit_shift_l
pluto_or
pluto_op
ACT
PRE
ACT
ACT
PRE
...

## Slide 72: More in the Paper
https://arxiv.org/pdf/2104.07699.pdf
Notes: YOU CAN FIND MORE DETAILS ABOUT OUR PROPOSED SYSTEM INTEGRATION STACK IN OUR PAPER,
INCLUDING A STEP-BY-STEP EXAMPLE OF HOW AN APPLICATION CHANGES FROM HIGH-LEVEL C CODE TO THE LOW-LEVEL PLUTO INSTRUCTIONS THAT MAP TO DRAM COMMANDS.

## Slide 73
Introduction
Evaluation
Conclusion
Contents
pLUTo
System Integration
pLUTo Designs
Overview

## Slide 74
Methodology: Experimental Setup
Baselines
  CPU (Intel® Xeon Gold 5118)
  GPU (NVIDIA® GeForce RTX 3080 Ti)
  Processing-near-Memory (PnM)
pLUTo
  In-house simulator, open-sourced
  https://github.com/CMU-SAFARI/pLUTo
We evaluate:
  Performance
  Energy consumption
  Area overhead
  Circuit-level reliability and correctness
  …

## Slide 75
Baselines
  CPU (Intel® Xeon Gold 5118)
  GPU (NVIDIA® GeForce RTX 3080 Ti)
  Processing-near-Memory (PnM)
pLUTo
  In-house simulator, open-sourced
  https://github.com/CMU-SAFARI/pLUTo
We evaluate:
  Performance
  Energy consumption
  Area overhead
  Circuit-level reliability and correctness
  …
Methodology: Experimental Setup
Notes: DUE TO TIME LIMITATIONS, I CAN ONLY COVER A SUBSET OF THESE, SO I WILL FOCUS ON PERFORMANCE AND ENERGY CONSUMPTION.

## Slide 76
Methodology: Workloads
7 real-world workloads (not well supported by prior work)
  CRC-8/16/32
  Salsa20
  VMPC
  Image Binarization
  Color Grading
4 synthetic workloads (supported by prior work)
  Vector Addition
  Vector Point-Wise Multiplication
  Row-Level Bitwise Logic Operations
  Bit Counting

## Slide 77
Average speedup across 7 real-world workloads
Performance
Chart: Average Speedup
| CPU | GPU | PnM
pLUTo-GSA | 357 | 0.6 | 9.2
pLUTo-BSA | 713 | 1.2 | 18.3
pLUTo-GMC | 1413 | 2.3 | 36.2
pLUTo significantly outperforms CPU, GPU and PnM baselines

## Slide 78
Average speedup normalized to area across 7 real-world workloads
Performance (normalized to area)
Chart: Average Speedup per Unit Area
| CPU | GPU | PnM
pLUTo-GSA | 426 | 441
pLUTo-BSA | 801 | 830
pLUTo-GMC | 1504 | 1558
pLUTo provides substantially higher performance per unit area than both the CPU and the GPU

## Slide 79
Average energy consumption across 7 real-world workloads
Energy Consumption
Chart: Average Energy Salving
| CPU | GPU | PnM
pLUTo-GSA | 1361.7035 | 28.9664
pLUTo-BSA | 1854.9695 | 39.4592
pLUTo-GMC | 3071.3751 | 65.3348
pLUTo significantly reduces energy consumption compared to processor-centric architectures for various workloads

## Slide 80: More Results in the Paper
Comparison with FPGA
Area Overhead Analysis
Circuit-Level Reliability & Correctness
Subarray-Level Parallelism
LUT Loading Overhead
Range of Supported Operations

## Slide 81
Introduction
Evaluation
Conclusion
Contents
pLUTo
System Integration
pLUTo Designs
Overview

## Slide 82
pLUTo Summary
The pLUTo Lookup Table Query introduces support for the execution of arbitrarily complex operations in DRAM
Notes: I WOULD NOW LIKE TO CONCLUDE BY SUMMARIZING PLUTO’S KEY POINTS.
PLUTO’S OPERATION IS RELIES ON THE PLUTO LUT QUERY, A NEWLY PROPOSED OPERATION THAT INTRODUCES SUPPORT FOR THE ARBITRARY EXECUTION OF COMPLEX OPERATIONS IN A PROCESSING-USING-MEMORY ARCHITECTURE.
WE INTRODUCED THREE DIFFERENT DESIGNS THAT EXPLOIT DIFFERENT TRADE-OFF POINTS IN PERFORMANCE, ENERGY EFFICIENCY AND AREA EFFICIENCY.
TO FACILITATE PROGRAMMER ADOPTION, WE THOROUGHLY DESCRIBE THE INTEGRATION OF THE PLUTO SUBSTRATE WITH THE HOST SYSTEM, WHICH ENCOMPASSES AN EASY-TO-USE API, A COMPILER, AND THE PLUTO CONTROLLER THAT CARRIES OUT COMPUTATION BY EXECUTING PLUTO ISA INSTRUCTIONS.

## Slide 83
pLUTo Summary
  Buffered Sense Amplifier, Gated Sense Amplifier & Gated Memory Cell target different performance/energy/area tradeoffs
The pLUTo Lookup Table Query introduces support for the execution of arbitrarily complex operations in DRAM
Notes: I WOULD NOW LIKE TO CONCLUDE BY SUMMARIZING PLUTO’S KEY POINTS.
PLUTO’S OPERATION IS RELIES ON THE PLUTO LUT QUERY, A NEWLY PROPOSED OPERATION THAT INTRODUCES SUPPORT FOR THE ARBITRARY EXECUTION OF COMPLEX OPERATIONS IN A PROCESSING-USING-MEMORY ARCHITECTURE.
WE INTRODUCED THREE DIFFERENT DESIGNS THAT EXPLOIT DIFFERENT TRADE-OFF POINTS IN PERFORMANCE, ENERGY EFFICIENCY AND AREA EFFICIENCY.
TO FACILITATE PROGRAMMER ADOPTION, WE THOROUGHLY DESCRIBE THE INTEGRATION OF THE PLUTO SUBSTRATE WITH THE HOST SYSTEM, WHICH ENCOMPASSES AN EASY-TO-USE API, A COMPILER, AND THE PLUTO CONTROLLER THAT CARRIES OUT COMPUTATION BY EXECUTING PLUTO ISA INSTRUCTIONS.

## Slide 84
pLUTo Summary
The pLUTo Lookup Table Query introduces support for the execution of arbitrarily complex operations in DRAM
  pLUTo API, pLUTo Compiler & pLUTo Controller
  facilitate programmer adoption of pLUTo
  Buffered Sense Amplifier, Gated Sense Amplifier & Gated Memory Cell target different performance/energy/area tradeoffs
Notes: I WOULD NOW LIKE TO CONCLUDE BY SUMMARIZING PLUTO’S KEY POINTS.
PLUTO’S OPERATION IS RELIES ON THE PLUTO LUT QUERY, A NEWLY PROPOSED OPERATION THAT INTRODUCES SUPPORT FOR THE ARBITRARY EXECUTION OF COMPLEX OPERATIONS IN A PROCESSING-USING-MEMORY ARCHITECTURE.
WE INTRODUCED THREE DIFFERENT DESIGNS THAT EXPLOIT DIFFERENT TRADE-OFF POINTS IN PERFORMANCE, ENERGY EFFICIENCY AND AREA EFFICIENCY.
TO FACILITATE PROGRAMMER ADOPTION, WE THOROUGHLY DESCRIBE THE INTEGRATION OF THE PLUTO SUBSTRATE WITH THE HOST SYSTEM, WHICH ENCOMPASSES AN EASY-TO-USE API, A COMPILER, AND THE PLUTO CONTROLLER THAT CARRIES OUT COMPUTATION BY EXECUTING PLUTO ISA INSTRUCTIONS.

## Slide 85
pLUTo Summary
The pLUTo Lookup Table Query introduces support for the execution of arbitrarily complex operations in DRAM
  Buffered Sense Amplifier, Gated Sense Amplifier & Gated Memory Cell target different performance/energy/area tradeoffs
  pLUTo API, pLUTo Compiler & pLUTo Controller
  facilitate programmer adoption of pLUTo
  pLUTo greatly outperforms the CPU/GPU/PnM baselines in performance and energy while incurring small area overheads
Notes: I WOULD NOW LIKE TO CONCLUDE BY SUMMARIZING PLUTO’S KEY POINTS.
PLUTO’S OPERATION IS RELIES ON THE PLUTO LUT QUERY, A NEWLY PROPOSED OPERATION THAT INTRODUCES SUPPORT FOR THE ARBITRARY EXECUTION OF COMPLEX OPERATIONS IN A PROCESSING-USING-MEMORY ARCHITECTURE.
WE INTRODUCED THREE DIFFERENT DESIGNS THAT EXPLOIT DIFFERENT TRADE-OFF POINTS IN PERFORMANCE, ENERGY EFFICIENCY AND AREA EFFICIENCY.
TO FACILITATE PROGRAMMER ADOPTION, WE THOROUGHLY DESCRIBE THE INTEGRATION OF THE PLUTO SUBSTRATE WITH THE HOST SYSTEM, WHICH ENCOMPASSES AN EASY-TO-USE API, A COMPILER, AND THE PLUTO CONTROLLER THAT CARRIES OUT COMPUTATION BY EXECUTING PLUTO ISA INSTRUCTIONS.

## Slide 86
Enabling Massively Parallel Computation in DRAM via Lookup Tables
João Dinis Ferreira |  | Gabriel Falcao |  | Juan Gómez-Luna |  | Mohammed Alser
Lois Orosa |  | Mohammad Sadrosadati |  | Jeremie S. Kim |  | Geraldo F. Oliveira
Taha Shahroodi |  | Anant Nori |  | Onur Mutlu
pLUTo
Notes: THIS CONCLUDES MY TALK. THANK YOU FOR YOUR ATTENTION, AND I AM HAPPY TO TAKE QUESTIONS.
<CLICK>

## Slide 87
pLUTo
Enabling Massively Parallel Computation in DRAM via Lookup Tables
arXiv
GitHub

## Slide 88
Enabling Massively Parallel Computation in DRAM via Lookup Tables
João Dinis Ferreira |  | Gabriel Falcao |  | Juan Gómez-Luna |  | Mohammed Alser
Lois Orosa |  | Mohammad Sadrosadati |  | Jeremie S. Kim |  | Geraldo F. Oliveira
Taha Shahroodi |  | Anant Nori |  | Onur Mutlu
pLUTo
Notes: THIS CONCLUDES MY TALK. THANK YOU FOR YOUR ATTENTION, AND I AM HAPPY TO TAKE QUESTIONS.
<CLICK>

## Slide 89
Backup Slides
Notes: THIS CONCLUDES MY TALK. THANK YOU FOR YOUR ATTENTION, AND I AM HAPPY TO TAKE QUESTIONS.
<CLICK>

## Slide 90: DRAM Organization

## Slide 91: pLUTo Components

## Slide 92: pLUTo Example Operation

## Slide 93: pLUTo Cell Designs

## Slide 94: System Integration: End-to-End

## Slide 95: Speedup

## Slide 96: Speedup Normalized to Unit Area

## Slide 97: Energy, Normalized

## Slide 98: Speedup Over FPGA

## Slide 99: Fraction of Time Spent Loading LUTs (DDR4, SSD) vs. Volume of Queried Data (MB)

## Slide 100: Comparison of Operations Supported by pLUTo vs. Prior Work

## Slide 101: Energy Efficiency (pLUTo vs. PuM vs. PnM) vs. Bit Width, one operation

## Slide 102: Throughput & Energy Consumption of pLUTo vs. LUT Query Size

## Slide 103: Speedup vs. Subarray-Level Parallelism

## Slide 104: Circuit-Level Reliability and Correctness

## Slide 105: Impact of tFAW

## Slide 106: QR Codes
arXiv
GitHub

## Slide 107
The pLUTo LUT Query: Backup
2 | 2 | 2 | 2
3 | 3 | 3 | 3
5 | 5 | 5 | 5
7 | 7 | 7 | 7
- | - | - | -
1 | 0 | 1 | 3
- | - | - | -
?
?
?
?
✓
0
Notes: TO ILLUSTRATE PLUTO’S OPERATION, I WILL NOW GO OVER THE EXECUTION OF A SIMPLE OPERATION IN PLUTO.
WE BEGIN BY CLEARLY DEFINING THE OPERATION WE WANT TO REPLACE.

## Slide 108: Banner Template
The quick brown fox jumps over the lazy dog