## Slide 1: AN EFFICIENT SYSTEM-LEVEL TECHNIQUE TO DETECT DATA-DEPENDENT FAILURES IN DRAM
Samira Khan
Donghyuk Lee
Onur Mutlu
PARBOR

## Slide 2: MEMORY IN TODAY’S SYSTEM
DRAM
Processor
Memory
Storage
DRAM is a critical for performance

## Slide 3: MAIN MEMORY CAPACITY
Gigabytes of DRAM
Increasing demand for high capacity
1. More cores
2. Data-intensive applications
How did we get more capacity?

## Slide 4: DRAM SCALING
Technology
Scaling
DRAM Cells
DRAM Cells
DRAM scaling enabled high capacity

## Slide 5: DRAM SCALING TREND
Technology
Scaling
DRAM Cells
DRAM Cells
More interference results in
more failures
Scaling places cells in close proximity,
increasing cell-to-cell interference

## Slide 6
How can we enable DRAM scaling
without sacrificing reliability?

## Slide 7: SYSTEM-LEVEL DETECTION AND MITIGATION
Detect and mitigate failures after
the system has become operational
Unreliable
DRAM Cells
Detect
and
Mitigate
Reliable System
Manufacturers can make cells smaller
without mitigating all failures

## Slide 8: SYSTEM-LEVEL DETECTION AND MITIGATION
Enables scalability [SIGMETRICS’14, DSN’14, DSN’15]
  Lets vendors manufacture smaller, unreliable cells
Improves reliability [ISCA’13, ISCA’14, DSN’14, DSN’15]
  Can detect failures that escape the manufacturing tests
Improves latency [HPCA’15, HPCA’16, SIGMETRICS’16]
  Reduces latency for cells that do not fail at lower latency
Enables refresh optimizations [ASPLOS’11, ISCA’12, DSN’15]
  Reduces refresh operations by using low refresh rate for robust cells

## Slide 9
CHALLENGE
System-level detection and mitigation
faces a major challenge due to
a specific type of failure:
DATA-DEPENDENT FAILURES

## Slide 10: DATA-DEPENDENT FAILURES
0
0
0
FAILURE
NO
FAILURE
1
1
INTERFERENCE
Some cells can fail depending on the
data stored in neighboring cells
JSSC’88, MDTD’02
Data-dependent failure is a major type
of cell-to-cell interference failure
Notes: Y. Nakagome, … Kiyoo Itoh, The Impact of Data-Line Interference Noise on DRAM Scaling, IJSSC’88
M. Redeker, B. F. Cockburn, and D. G. Elliott. An investigation into crosstalk noise in DRAM structures. MTDT, 2002 (Memory Technology, Design and Testing)
J. Liu et al. An experimental study of data retention behavior in modern DRAM devices: Implications for retention time profiling mechanisms, ISCA 2012

## Slide 11: CHALLENGE IN DETECTING DATA-DEPENDENT FAILURES
Detect failures by writing specific patterns
in the neighboring cell addresses
LINEAR
ADDRESS
X-1
X
X+1
L
D
R
PROBLEM: Scrambled address is not
visible to system (e.g. memory controller)
0
1
0
SCRAMBLED
ADDRESS
X-4
X
X+2
0
1
0
0
1
0
X-1
X+1

## Slide 12: CAN WE DETERMINE THE LOCATION OF PHYSICALLY ADJACENT CELLS?
NAÏVE SOLUTION
For a given failure X,
test every combination of two bit addresses in the row
Not feasible in a real system
O(n2)
8192*8192 tests, 49 days for a row with 8K cells
SCRAMBLED
ADDRESS
X-?
X
X+?
L
D
R

## Slide 13: OUR APPROACH: PARBOR
Goal:
A fast and efficient way to determine the locations of neighboring cells

## Slide 14: PARBOR: Summary
Reduces test time using two key ideas:
Exploits heterogeneity in cell interference to reduce test time by detecting only one neighbor
Exploits DRAM regularity and parallelism to detect all neighbor locations by running parallel tests in multiple rows
Detects neighboring locations
within 60-99 tests in 144 real DRAM chips,
a 745,654X reduction compared to naïve tests
A new technique to determine
the locations of neighboring DRAM cells

## Slide 15: OUTLINE
Data-Dependent Failures
Challenges in System-Level Detection
Our Mechanism: PARBOR
Experimental Results from Real Chips
Use Cases

## Slide 16: A DRAM cell
Capacitor
Transistor
Contact
Transistor
Bitline
Capacitor
Bitline
LOGICAL VIEW
VERTICAL CROSS SECTION
A DRAM CELL

## Slide 17: DATA-DEPENDENT FAILURES
Failures depend on the data content
in neighboring cells
Indirect path
Indirect path
Coupled Cells
0
1
0
Notes: Due to coupling effect in DRAM, neighboring cells provide an indirect path that can interfere with the charge stored in cells. AS a result cells can fail based on the content in the neighboring cells.
For example, here when the neighboring cells are storing 010, the middle cell can lose charge due to coupling between cells and can result in a failure.

## Slide 18: DETECTING DATA-DEPENDENT FAILURES
X-1
X
X+1
L
D
R
Need to write specific data patterns
in neighboring addresses
0
1
0
To test cell at address X, write 1 at address X and 0s at address X+1 and X-1

## Slide 19: OUTLINE
Data-Dependent Failures
Challenges in System-Level Detection
Our Mechanism: PARBOR
Experimental Results from Real Chips
Use Cases

## Slide 20: CHALLENGE: SCRAMBLED ADDRESS SPACE
SCRAMBLED
ADDRESS
X-4
X
X+2
0
1
0
0
1
0
X-1
X+1
SCRAMBLED
ADDRESS
X-?
X
X+?
0
1
0
Scrambled address not visible to system
Cannot detect failures without the address mapping information

## Slide 21: CHALLENGE: SCRAMBLED ADDRESS SPACE
Different for each generation and vendor
Need a dynamic way to detect address mapping information in the system
SCRAMBLED
ADDRESS
X-2
X
X+5
0
1
0
SCRAMBLED
ADDRESS
X-4
X
X+2
0
1
0
0
1
0
Vendor A
Vendor B

## Slide 22: NAIVE SOLUTION
Determine the location of neighboring cells
NAÏVE SOLUTION: O(n2)
For a given failure X, test every combination of two bit addresses in the row
  Address bits: (0, 0), (0, 1), … (X-1, X), (X, X+1) ... (n-1, n)
For vendor A
  X will fail only when X-4, X+2 tested
8192*8192 tests, 49 days for a row with 8K cells
Not feasible in a real system
SCRAMBLED
ADDRESS
X-?
X
X+?
L
D
R

## Slide 23
A fast and efficient way
to determine
the locations of neighboring cells
GOAL

## Slide 24: OUTLINE
Data-Dependent Failures
Challenges in System-Level Detection
Our Mechanism: PARBOR
Experimental Results from Real Chips
Use Cases

## Slide 25: PARBOR: KEY OBSERVATIONS
Key observation 1:
Data-dependent failures depend on the heterogeneity in coupled cells
  Some cells are strongly coupled and fail based on the data content in just one neighbor
  Reduce test time by detecting only one neighbor
CHALLENGE: Detecting failures with only one neighbor information cannot find all failures
Reduces test time based on two key observations:

## Slide 26: PARBOR: KEY OBSERVATIONS
Key observation 2:
DRAM exhibits regularity and parallelism
  Neighbors are located at the same distance in different rows of DRAM
  Detect all neighbor locations by running parallel tests in multiple rows
Reduces test time based on two key observations:

## Slide 27: KEY OBSERVATION 1: STRONGLY VS. WEAKLY COUPLED CELLS
STRONGLY COUPLED CELL
Fails even if only one neighbor’s data changes
WEAKLY COUPLED CELL
Fails if both neighbors’ data change

## Slide 28: KEY IDEA 1: EXPLOITING STRONGLY COUPLED CELLS
Instead of detecting both neighbors, reduce test time by detecting only one neighbor location in strongly coupled cells
  Does not need to detect every two bit addresses
  Linearly tests every bit address
  0, 1, … , X, X+1, X+2, … n
ADVANTAGES
Reduces test time to linear O(n)
Can reduce test time further by applying recursive tests to linear tests
SCRAMBLED
ADDRESS
X
X-?
L
A
R

## Slide 29: RECURSIVE TEST
LINEAR
TESTING
0 1 2 3 4 5 6 7
RECURSIVE
TESTING
0, 1, 2, 3
0
1
4, 5
2
3
4
5
2, 3
0, 1
6
7
SCRAMBLED
ADDRESS
X-4
L
A
4, 5, 6, 7
6, 7
X
2
6
Recursive test reduces test time
compared to linear testing

## Slide 30
CHALLENGE:
Detecting failures with
only one neighbor information cannot find
*all* data-dependent failures

## Slide 31: PARBOR: KEY OBSERVATIONS
Key observation 1:
Data-dependent failures depend on the heterogeneity in coupled cells
  Some cells are strongly coupled and fail based on the data content in just one neighbor
  Reduce test time by detecting only one neighbor
Key observation 2:
DRAM exhibits regularity and parallelism
  Neighbors are located at the same distance in different rows of DRAM
  Detect all neighbor locations by running parallel tests in multiple rows
Reduces test time based on two key observations:

## Slide 32: KEY OBSERVATION 2: REGULARITY AND PARALLELISM IN DRAM
DRAM Bank
A
B
C
D
+1
+5
+1
+1
+1
+5
+5
+5
DRAM Tile
DRAM is internally organized as a 2D array of similar and repetitive tiles.
This regularity results in
regularity in address mapping

## Slide 33: KEY OBSERVATION 2: REGULARITY AND PARALLELISM IN DRAM
1 0 5 4 9 8 3 2 7 6 11 10
±1 ±5 ±1 ±5 ±1 ±1 ±5 ±1 ±5 ±1
DRAM Tile
SYSTEM
ADDRESS
Due to regularity in tiles, neighbors can occur only in fixed distances

## Slide 34: KEY OBSERVATION 2: REGULARITY AND PARALLELISM IN DRAM
A
D
B
C
1 0 5 4 9 8 3 2 7 6 11 10
±1 ±5 ±1 ±5 ±1 ±1 ±5 ±1 ±5 ±1
+1
+5
+1
+5
-5
-1
-1
-5
DRAM Tile
SYSTEM
ADDRESS
A, B, C, D provide all neighbor distances
{+1, -5, +5, -1}

## Slide 35: KEY IDEA 2: PARALLEL TESTS IN MULTIPLE ROWS
Due to regularity in mapping, it is possible to determine the neighbor locations from different rows
Run parallel tests in multiple rows
Detect the neighbors’ distances in these rows
Aggregate the locations from different rows
Provides the neighbor distances for all cells

## Slide 36: KEY IDEA 2: PARALLEL TESTS IN MULTIPLE ROWS
A
D
B
C
1 0 5 4 9 8 3 2 7 6 11 10
±1 ±5 ±1 ±5 ±1 ±1 ±5 ±1 ±5 ±1
+5
-5
-1
DRAM Tile
SYSTEM
ADDRESS
Aggregated neighbor locations {+1, -5, +5, -1}
A+1
B-5
C-1
D+5
+1

## Slide 37: OUTLINE
Data-Dependent Failures
Challenges in System-Level Detection
Our Mechanism: PARBOR
Experimental Results from Real Chips
Use Cases

## Slide 38: METHODOLOGY
Evaluated 144 chips from three major vendors
An FPGA-based testing infrastructure
[ISCA’13, SIGMETRICS’14, ISCA’14, HPCA’15, DSN’15, SIGMETRICS’16]

## Slide 39: PARBOR: TEST CHARACTERISTICS
A
B
C
NUM TEST
REDUCED
745654X
1016800X
745654X
Can detect neighbor locations
in 66-90 tests

## Slide 40: PARBOR: TEST CHARACTERISTICS
±8, ±16, ±48
±1, ±64
±16, ±33, ±49
A
B
C
NEIGHBOR LOCATIONS
NUM TEST
REDUCED
745654X
1016800X
745654X
Can detect different address mapping in different chips

## Slide 41: OUTLINE
Data-Dependent Failures
Challenges in System-Level Detection
Our Mechanism: PARBOR
Experimental Results from Real Chips
Use Cases

## Slide 42: USE CASES
USE CASE: PHYSICAL NEIGHBOR AWARE TEST
Use neighbor information to efficiently detect all data-dependent failures
USE CASE: DATA-CONTENT BASED REFRESH
Use neighbor information and program content to reduce refresh count

## Slide 43: USE CASE: PHYSICAL NEIGHBOR-AWARE TEST
Use neighbor information to efficiently detect all data-dependent failures
Use PARBOR to detect neighbor locations
  Neighbor locations at {±1 ±5}
Can test every 11 bits in parallel
  Reduces test time, needs only 11 tests
At each test, write data pattern at the neighboring cells of each address
  X-5, X+1, X, X-1, X+5 --> 0, 0, 1, 0, 0

## Slide 44: USE CASE: PHYSICAL NEIGHBOR-AWARE TEST
42%
7%
18%
A
B
C
EXTRA FAILURES
DETECTED
NUM TESTS
32
32
16
Detects more failures
with small number of tests
leveraging neighboring information

## Slide 45: USE CASES
USE CASE: PHYSICAL NEIGHBOR AWARE TEST
Use neighbor information to efficiently detect all data-dependent failures
USE CASE: DATA-CONTENT BASED REFRESH
Use neighbor information and program content to reduce refresh count

## Slide 46: PROBLEM WITH TRADITIONAL REFRESH OPTIMIZATION
Does not take into account that
failures occur only with specific content
Traditional refresh optimization: [RAIDR ISCA’12]
  High refresh rate with rows with failures
  Low refresh rate for rows with no failure
Hi-REF
Lo-REF
Lo-REF
Lo-REF

## Slide 47: A NEW USE CASE: DATA-CONTENT AWARE REFRESH
DC-REF optimization:
  Builds on top of PARBOR to track locations of data-dependent failures and data patterns that cause the failures
  High refresh rate for rows whose data content exhibits failures
  Low refresh rate for rows with no failure
0
1
0
Hi-REF only when contains 010
Lo-REF
Lo-REF
Lo-REF

## Slide 48: DATA-CONTENT AWARE REFRESH: Fraction of Rows with High Refresh Rate
DC-REF significantly reduces
the number of high refresh operations
Chart: Fraction of Rows with Hi-REF
| 4.0
RAIDR | 16.4
DC-REF | 2.7
2.7%
16.4%

## Slide 49: DATA-CONTENT AWARE REFRESH: PREFORMANCE IMPACT
DC-REF improves performance by reducing refresh operations
Chart: DRAM Chip Capacity (Gbit)
| 4.0 | 8.0 | 16.0 | 32.0
RAIDR | 4.5259 | 5.8812 | 9.3875 | 15.0383
DC-REF | 5.3111 | 6.917 | 11.1057 | 17.9605

## Slide 50: PARBOR: Summary
Exploits heterogeneity in data-dependent cells to reduce test time by detecting only one neighbor
Exploits DRAM regularity and parallelism to aggregate neighbor locations from multiple rows to identify all neighbor locations
Enables new uses cases to improve performance, reliability, and energy efficiency
  Physical neighbor-aware test
  Data-content aware refresh
A new technique to determine
the locations of neighboring DRAM cells

## Slide 51: AN EFFICIENT SYSTEM-LEVEL TECHNIQUE TO DETECT DATA-DEPENDENT FAILURES IN DRAM
Samira Khan
Donghyuk Lee
Onur Mutlu
PARBOR

## Slide 52: USE CASE: PHYSICAL NEIGHBOR-AWARE TEST
A
B
C
Chart: 
| Common | Only in Random Test | Only in Coupling-Aware Test
 | 81.0884 | 5.3566 | 13.555
Chart: 
| Common | Only in Random Test | Only in Coupling-Aware Test
 | 79.0936 | 0.53611 | 20.3703
 | 69.4318 | 0.91616 | 29.6521
Chart: 
| Common | Only in Random Test | Only in Coupling-Aware Test
 | 69.4318 | 0.91616 | 29.6521
 | 69.4318 | 0.91616 | 29.6521
 | 69.4318 | 0.91616 | 29.6521
 | 69.4318 | 0.91616 | 29.6521
A significant fraction of failures
can be detected only by PARBOR (20-30%)