## Slide 1: Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency
Gennady Pekhimenko
Advisers: Todd C. Mowry & Onur Mutlu

## Slide 2: Executive Summary
Main memory is a limited shared resource
Observation: Significant data redundancy
Idea: Compress data in main memory
Problem: How to avoid latency increase?
Solution: Linearly Compressed Pages (LCP):
fixed-size cache line granularity compression
1. Increases capacity (69% on average)
2. Decreases bandwidth consumption (46%)
3. Improves overall performance (9.5%)

## Slide 3: Challenges in Main Memory Compression
Address Computation
Mapping and Fragmentation
Physically Tagged Caches

## Slide 4: Address Computation
L0
L1
L2
. . .
LN-1
Cache Line (64B)
Address Offset
0
64
128
(N-1)*64
L0
L1
L2
. . .
LN-1
Compressed Page
0
?
?
?
Address Offset
Uncompressed Page

## Slide 5: Mapping and Fragmentation
Virtual Page
(4kB)
Physical Page
(? kB)
Fragmentation
Virtual
Address
Physical
Address

## Slide 6: Physically Tagged Caches
Core
TLB
tag
tag
tag
Physical Address
data
data
data
Virtual
Address
Critical Path
Address Translation
L2 Cache
Lines

## Slide 7: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 

## Slide 8: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 

## Slide 9: Shortcomings of Prior Work
Compression Mechanisms | Access Latency | Decompression Latency | Complexity | Compression Ratio
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 
LCP: Our Proposal |  |  |  | 

## Slide 10: Linearly Compressed Pages (LCP): Key Idea
64B
64B
64B
64B
. . .
. . .
M
E
Metadata (64B):
? (compressible)
Exception
Storage
4:1 Compression
64B
Uncompressed Page (4kB: 64*64B)
Compressed Data
(1kB)

## Slide 11: LCP Overview
Page Table entry extension
  compression type and size
  extended physical base address
Operating System management support
  4 memory pools (512B, 1kB, 2kB, 4kB)
Changes to cache tagging logic
  physical page base address + cache line index
  (within a page)
Handling page overflows
Compression algorithms: BDI [PACT’12] , FPC [ISCA’04]

## Slide 12: LCP Optimizations
Metadata cache
  Avoids additional requests to metadata
Memory bandwidth reduction:
Zero pages and zero cache lines
  Handled separately in TLB (1-bit) and in metadata
  (1-bit per cache line)
Integration with cache compression
  BDI and FPC
64B
64B
64B
64B
1 transfer
instead of 4

## Slide 13: Methodology
Simulator
  x86 event-driven simulators
    Simics-based [Magnusson+, Computer’02] for CPU
    Multi2Sim [Ubal+, PACT’12] for GPU
Workloads
  SPEC2006 benchmarks, TPC, Apache web server, GPGPU applications
System Parameters
  L1/L2/L3 cache latencies from CACTI [Thoziyoor+, ISCA’08]
  512kB - 16MB L2, simple memory model

## Slide 14: Compression Ratio Comparison
Chart: GeoMean
| GeoMean
Zero Page | 1.2982
FPC | 1.5908
LCP (BDI) | 1.6239
LCP (BDI+FPC-fixed) | 1.6909
MXT | 2.3051
LZ | 2.6049
SPEC2006, databases, web workloads, 2MB L2 cache
LCP-based frameworks achieve competitive average compression ratios with prior work

## Slide 15: Bandwidth Consumption Decrease
SPEC2006, databases, web workloads, 2MB L2 cache
Chart: Normalized BPKI
| GeoMean
FPC-cache | 0.92005
BDI-cache | 0.89057
FPC-memory | 0.57215
(None, LCP-BDI) | 0.62549
(FPC, FPC) | 0.5362
(BDI, LCP-BDI) | 0.55124
(BDI, LCP-BDI+FPC-fixed) | 0.53836
LCP frameworks significantly reduce bandwidth (46%)
Better
Notes: BPKI – bandwidth per kilo instruction – lower means better.

## Slide 16: Performance Improvement
Cores | LCP-BDI | (BDI, LCP-BDI) | (BDI, LCP-BDI+FPC-fixed)
1 | 6.1% | 9.5% | 9.3%
2 | 13.9% | 23.7% | 23.6%
4 | 10.7% | 22.6% | 22.5%
LCP frameworks significantly improve performance

## Slide 17: Conclusion
A new main memory compression framework called LCP(Linearly Compressed Pages)
  Key idea: ﬁxed size for compressed cache lines within a page and fixed compression algorithm per page
LCP evaluation:
  Increases capacity (69% on average)
  Decreases bandwidth consumption (46%)
  Improves overall performance (9.5%)
  Decreases energy of the off-chip bus (37%)

## Slide 18: Linearly Compressed Pages: A Main Memory Compression Framework with Low Complexity and Low Latency
Gennady Pekhimenko
Advisers: Todd C. Mowry & Onur Mutlu