## Slide 1: PIM-Enabled Instructions: A Low-Overhead, Locality-Aware PIM Architecture
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu+, and Kiyoung Choi
Seoul National University
+Carnegie Mellon University

## Slide 2: Processing-in-Memory
Move computation to memory
  Higher memory bandwidth
  Lower memory latency
  Better energy efficiency (e.g., off-chip links vs. TSVs)
Originally studied in 1990s
  Also known as processor-in-memory
  e.g., DIVA, EXECUBE, FlexRAM, IRAM, Active Pages, …
  Not commercialized in the end
Why was PIM unsuccessful in its first attempt?

## Slide 3: Challenges in Processing-in-Memory
DRAM die
Cost-effectiveness
Programming Model
Coherence & VM
DRAM die
Complex Logic
Host Processor
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
In-Memory Processors
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Host Processor
3
3
4
5
C
C

## Slide 4: Challenges in Processing-in-Memory
DRAM die
Cost-effectiveness
Programming Model
Coherence & VM
DRAM die
Complex Logic
Host Processor
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
In-Memory Processors
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Thread
Host Processor
3
3
4
5
C
C
(Partially) Solved by
3D-Stacked DRAM
Still Challenging even in Recent PIM Architectures
(e.g., AC-DIMM, NDA, NDC, TOP-PIM, Tesseract, …)

## Slide 5: New Direction of PIM
Objectives
  Provide an intuitive programming model for PIM
  Full support for cache coherence and virtual memory
  Reduce the implementation overhead of PIM units
Our solution: simple PIM operations as ISA extension
  Simple: low-overhead implementation
  PIM operations as host processor instructions: intuitive
  Conventional PIM : Simple PIM ≈ GPGPU : SSE/AVX

## Slide 6: Potential of ISA Extension as PIM Interface
Example: Parallel PageRank computation
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}
for (v: graph.vertices) {
v.rank = v.next_rank; v.next_rank = alpha;
}

## Slide 7: Potential of ISA Extension as PIM Interface
Main Memory
w.next_rank
w.next_rank
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}
Host Processor
w.next_rank
w.next_rank
64 bytes in
64 bytes out
Conventional Architecture

## Slide 8: Potential of ISA Extension as PIM Interface
Main Memory
w.next_rank
w.next_rank
Host Processor
value
8 bytes in
0 bytes out
In-Memory Addition
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pim.add r1, (r2)

## Slide 9: Potential of ISA Extension as PIM Interface
Chart: Speedup
| p2p-Gnu tella31 | soc-Slash dot0811 | web- Stanford | amazon- 2008 | frwiki- 2013 | wiki- Talk | cit- Patents | soc-Live Journal1 | ljournal- 2008
계열 1 | -0.19828 | -0.072364 | -0.11014 | -0.0073164 | 0.015521 | 0.30554 | 0.53667 | 0.50416 | 0.18676
More Vertices
Increase in Memory Bandwidth Consumption Lack of On-Chip Caches
Reduction in Memory Bandwidth Consumption
In-Memory Computation

## Slide 10: Overview
How should simple PIM operations be interfaced to conventional systems?
  Expose PIM operations as cache-coherent, virtually-addressed host processor instructions
  No changes to the existing sequential programming model
What is the most efficient way of exploiting such simple PIM operations?
  Dynamically determine the location of PIM execution based on data locality without software hints

## Slide 11: PIM-Enabled Instructions
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
w.next_rank += value;
}
}

## Slide 12: PIM-Enabled Instructions
Executed either in memory or in the host processor
Cache-coherent, virtually-addressed
Atomic between different PEIs
Not atomic with normal instructions (use pfence)
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pim.add r1, (r2)

## Slide 13: PIM-Enabled Instructions
Executed either in memory or in the host processor
Cache-coherent, virtually-addressed
Atomic between different PEIs
Not atomic with normal instructions (use pfence)
for (v: graph.vertices) {
value = weight * v.rank;
for (w: v.successors) {
__pim_add(&w.next_rank, value);
}
}
pfence();
pim.add r1, (r2)
pfence

## Slide 14: PIM-Enabled Instructions
Key to practicality: single-cache-block restriction
  Each PEI can access at most one last-level cache block
  Similar restrictions exist in atomic instructions
Benefits
  Localization: each PEI is bounded to one memory module
  Interoperability: easier support for cache coherence and virtual memory
  Simplified locality monitoring: data locality of PEIs can be identified by LLC tag checks or similar methods

## Slide 15: Architecture
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
Proposed PEI Architecture

## Slide 16: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
y

## Slide 17: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
y
Address Translation for PEIs
Done by the host processor TLB (similar to normal instructions)
No modifications to existing HW/OS
No need for in-memory TLBs

## Slide 18: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
y
Wait until x is writable

## Slide 19: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
Wait until x is writable
Reader-writer lock #0
Reader-writer lock #1
Reader-writer lock #N-1
Reader-writer lock #2
…
Address
XOR-Hash
(Inexact, but Conservative)

## Slide 20: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
Wait until x is writable
Check the data locality of x
y

## Slide 21: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
Wait until x is writable
Check the data locality of x
y
Hit: High locality
Miss: Low locality
Tag
Tag
Tag
Tag
…
Tag
Tag
Tag
Tag
…
Tag
Tag
Tag
Tag
…
…
Address
Partial Tag Array
Updated on
Each LLC access
Each issue of a PIM operation to memory

## Slide 22: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
y
x
Low locality
Wait until x is writable
Check the data locality of x

## Slide 23: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
y
x
Low locality
Back-invalidation for cache coherence
No modifications to existing cache coherence protocols

## Slide 24: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
y
x
x+y
y
x+y
Low locality

## Slide 25: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
y
x+y
x+y
Completely Localized PIM Memory Accesses without Special Data Mapping

## Slide 26: Memory-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
y
x
x+y
x+y
Completion Notification

## Slide 27: Host-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
y
Wait until x is writable
Check the data locality of x

## Slide 28: Host-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
Wait until x is writable
Check the data locality of x
x
High locality
x
x+y
x
x+y

## Slide 29: Host-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
x+y
x
x
x+y
No Cache Coherence Issues

## Slide 30: Host-side PEI Execution
Out-Of-Order Core
L1 Cache
L2 Cache
Last-Level Cache
HMC Controller
Crossbar Network
DRAM Controller
DRAM Controller
DRAM Controller
Host Processor
HMC
…
PCU
PCU
PCU
PCU
PIM Directory
Locality Monitor
PMU
pim.add y, &x
x
y
x+y
x
x
x+y
Completion Notification

## Slide 31: Mechanism Summary
Atomicity of PEIs
  PIM directory implements reader-writer locks
Locality-aware PEI execution
  Locality monitor simulates cache replacement behavior
Cache coherence for PEIs
  Memory-side: back-invalidation/back-writeback
  Host-side: no need for consideration
Virtual memory for PEIs
  Host processor performs address translation before issuing a PEI

## Slide 32: Simulation Configuration
In-house x86-64 simulator based on Pin
  16 out-of-order cores, 4GHz, 4-issue
  32KB private L1 I/D-cache, 256KB private L2 cache
  16MB shared 16-way L3 cache, 64B blocks
  32GB main memory with 8 daisy-chained HMCs (80GB/s)
PCU
  1-issue computation logic, 4-entry operand buffer
  16 host-side PCUs at 4GHz, 128 memory-side PCUs at 2GHz
PMU
  PIM directory: 2048 entries (3.25KB)
  Locality monitor: similar to LLC tag array (512KB)

## Slide 33: Target Applications
Ten emerging data-intensive workloads
  Large-scale graph processing
    Average teenage followers, BFS, PageRank, single-source shortest path, weakly connected components
  In-memory data analytics
    Hash join, histogram, radix partitioning
  Machine learning and data mining
    Streamcluster, SVM-RFE
Three input sets (small, medium, large) for each workload to show the impact of data locality

## Slide 34: Speedup
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.53918 | 0.31004 | 0.50416 | 0.45845 | 0.47598 | 0.66307 | 0.6314 | 0.44904 | 0.15358 | 0.33671 | 0.4446
Locality-Aware | 0.60067 | 0.34622 | 0.55934 | 0.51064 | 0.5286 | 0.65698 | 0.60316 | 0.44327 | 0.2149 | 0.3438 | 0.47446
(Large Inputs, Baseline: Host-Only)

## Slide 35: Speedup
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.53918 | 0.31004 | 0.50416 | 0.45845 | 0.47598 | 0.66307 | 0.6314 | 0.44904 | 0.15358 | 0.33671 | 0.4446
Locality-Aware | 0.60067 | 0.34622 | 0.55934 | 0.51064 | 0.5286 | 0.65698 | 0.60316 | 0.44327 | 0.2149 | 0.3438 | 0.47446
(Large Inputs, Baseline: Host-Only)
Chart: Normalized Amount of Off-chip Transfer
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM
Host-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Only | 0.57082 | 0.75659 | 0.68201 | 0.74528 | 0.69303 | 0.7343 | 0.66669 | 0.82187 | 1.066 | 1.0402
Locality-Aware | 0.53033 | 0.70259 | 0.58305 | 0.62293 | 0.61429 | 0.73496 | 0.66669 | 0.82173 | 1.0575 | 0.9762

## Slide 36: Speedup
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | -0.22001 | -0.17526 | -0.072364 | -0.074298 | -0.090338 | -0.20025 | 0.54727 | -0.50008 | -0.40915 | -0.43574 | -0.20283
Locality-Aware | 0.050393 | 0.033552 | 0.00024264 | 0.0089585 | 0.0094162 | -0.013054 | 0.51424 | -0.0057565 | -0.0011447 | -0.0029887 | 0.05049
(Small Inputs, Baseline: Host-Only)

## Slide 37: Speedup
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | -0.22001 | -0.17526 | -0.072364 | -0.074298 | -0.090338 | -0.20025 | 0.54727 | -0.50008 | -0.40915 | -0.43574 | -0.20283
Locality-Aware | 0.050393 | 0.033552 | 0.00024264 | 0.0089585 | 0.0094162 | -0.013054 | 0.51424 | -0.0057565 | -0.0011447 | -0.0029887 | 0.05049
(Small Inputs, Baseline: Host-Only)
Chart: Normalized Amount of Off-chip Transfer
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM
Host-Only | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
PIM-Only | 2.2436 | 2.8887 | 3.1716 | 6.4881 | 3.6498 | 3.5416 | 0.67043 | 16.241 | 501.6688 | 408.0847
Locality-Aware | 1.1309 | 1.1806 | 1.0027 | 1.123 | 1.0907 | 1.1189 | 0.67043 | 1.038 | 1.7717 | 2.5209
16.1
502
408

## Slide 38: Speedup
Chart: 
| ATF | BFS | PR | SP | WCC | HJ | HG | RP | SC | SVM | GM
PIM-Only | 0.016737 | -0.013893 | 0.015521 | 0.03812 | 0.0073854 | 0.22636 | 0.62757 | 0.2138 | 0.077582 | -0.034224 | 0.1038
Locality-Aware | 0.13541 | 0.1263 | 0.11073 | 0.12106 | 0.13711 | 0.17555 | 0.59989 | 0.21386 | 0.13909 | 0.0445 | 0.17268
(Medium Inputs, Baseline: Host-Only)

## Slide 39: Sensitivity to Input Size
Chart: Speedup
| p2p-Gnu tella31 | soc-Slash dot0811 | web- Stanford | amazon- 2008 | frwiki- 2013 | wiki- Talk | cit- Patents | soc-Live Journal1 | ljournal- 2008
PIM-Only | -0.19828 | -0.072364 | -0.11014 | -0.0073164 | 0.015521 | 0.30554 | 0.53667 | 0.50416 | 0.18676
Locality-Aware | -0.0032363 | 0.00024264 | 0.033693 | 0.066601 | 0.11073 | 0.35266 | 0.52496 | 0.55934 | 0.19881
PIM % | 0.030075 | 0.0032358 | 0.14551 | 0.29868 | 0.17744 | 0.73435 | 0.87487 | 0.58999 | 0.27209

## Slide 40: Multiprogrammed Workloads
Chart: 
Host-Only

## Slide 41: Energy Consumption
Chart: 
| Small | Medium | Large
Cache | 0.27613 | 0.22974 | 0.2138
HMC Link | 0.50415 | 0.51297 | 0.51397
DRAM | 0.21457 | 0.25453 | 0.26887
Host-side PCU | 0.0043662 | 0.0036967 | 0.0030358
Memory-side PCU | 0 | 0 | 0
PMU | 7.7323e-05 | 6.4146e-05 | 5.4225e-05
계열 7 | 0.29322 | 0.18897 | 0.14107
계열 8 | 0.68428 | 0.4834 | 0.36147
계열 9 | 0.46391 | 0.35056 | 0.26204
계열 10 | 0 | 0 | 0
계열 11 | 0.015795 | 0.011518 | 0.0085371
계열 12 | 0.0053637 | 0.0036921 | 0.0027686
Host-Only
PIM-Only
Locality-Aware

## Slide 42: Conclusion
Challenges of PIM architecture design
  Cost-effective integration of logic and memory
  Unconventional programming models
  Lack of interoperability with caches and virtual memory
PIM-enabled instruction: low-cost PIM abstraction & HW
  Interfaces PIM operations as ISA extension
  Simplifies cache coherence and virtual memory support for PIM
  Locality-aware execution of PIM operations
Evaluations
  47%/32% speedup over Host/PIM-Only in large/small inputs
  Good adaptivity across randomly generated workloads

## Slide 43: PIM-Enabled Instructions: A Low-Overhead, Locality-Aware PIM Architecture
Junwhan Ahn, Sungjoo Yoo, Onur Mutlu+, and Kiyoung Choi
Seoul National University
+Carnegie Mellon University