## Slide 1
Proteus Achieving High-Performance Processing-Using-DRAM with Dynamic Bit-Precision, Adaptive Data Representation, and Flexible Arithmetic
Geraldo F. Oliveira |  |  | 
Mayank Kabra | Yuxin Guo | Kangqi Chen | Giray Yağlıkçı
Melina Soysal | Mohammad Sadr | Joaquin O. Bueno | Saugata Ghose
Juan Gómez-Luna |  | Onur Mutlu | 
2025 International Conference on Supercomputing (ICS)
Notes: Hi, I am Geraldo, a PhD graduate at the SAFARI Research Group.
Today, I will talk about our work Proteus: Achieving High-Performance Processing-Using-DRAM with Dynamic Bit-Precision, Adaptive Data Representation, and Flexible Arithmetic So, let’s get started.
[NEXT]

## Slide 2: Executive Summary
Key Mechanism: Proteus, a data-aware runtime PUD framework that
dynamically adjust the bit-precision
chooses and uses the most appropriate data representation and arithmetic algorithm implementation
for a given PUD operation
Goal: Design a PUD system that overcomes the three limitations caused by naively employing a bit-serial execution model
Key Results: Proteus achieves
17x (90.3x), 7.3x (21x), and 10.2x (8.1x) the performance per mm2 (energy reduction) of a high-end CPU, GPU, and state-of-the-art PUD system
Small area cost to a DRAM chip (1.6%) and CPU die (0.03%)
Problem: Processing-Using-DRAM (PUD) suffers from three limitations caused by naive employing a bit-serial execution model
Rigid and static data representation leading to unnecessary computation
Throughput-oriented execution leading to limited latency tolerance
Scalability challenges for high-precision operations
https://github.com/CMU-SAFARI/Proteus
Notes: Before we start, I will give a summary of OUR work.
Processing-in-memory architectures are emerging solutions to mitigate data movement bottlenecks by moving computation where the data resides. In particular, processing using DRAM is a PIM architecture that utilizes DRAM’s analog operating principles to implement bulk operations.
[CLICK] Even though processing-using-DRAM can often accelerate many application domains, they suffer from three issues caused by naively employing a bit-serial execution model
[CLICK] First, they suffer from a rigid and static data representation, leading to unnecessary computation in the presence of narrow values
[CLICK] Second, they a throughput-oriented execution with limited latency tolerance
[CLICK] Third, they suffer from scalability challenges for high-precision arithmetic operations
[CLICK] Therefore, our goal in this work is to design a PUD system that overcomes the three limitations caused by naively employing a bit-serial execution model
[CLICK] To this end, we propose Proteus, a data-aware runtime PUD framework that dynamically adjust the bit-precision of PUD operations, and based on that chooses and uses the most appropriate data representation and arithmetic algorithm implementation.
[CLICK[ We extensively evaluation Proteus, and we observe that it achieves significant performance and energy efficiency gains compared to state-of-the-art PUD systems, a high-end CPU and GPU
while incurring low area cost to a DRAM chip and CPU die.
[NEXT]

## Slide 3: Outline
Introduction
1
Background
2
PUD’s Limitations & Key Ideas
3
Proteus
4
Evaluation
5
Conclusion
6
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: This is the outline for my talk.
First …
[NEXT]

## Slide 4: Outline
Introduction
1
Background
2
PUD’s Limitations & Key Ideas
3
Proteus
4
Evaluation
5
Conclusion
6
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: So let’s get started.
[NEXT]

## Slide 5: Processing-in-Memory: Overview (I)
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
…
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks by moving computation to where the data resides. Such architectures can be implemented
[CLICK] by adding logic near the memory arrays, in what is called processing-near-memory or
[CLICK] by using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
[NEXT]

## Slide 6: Processing-in-Memory: Overview (II)
Processing-Near-Bank
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
Processing-Near-Vault
DRAM Vault
  Two main approaches for Processing-in-Memory:
1
Processing-Near-Memory: PIM logic is added to the same die as memory or to the logic layer of 3D-stacked memory
…
2
Processing-Using-Memory: uses the operational principles of memory cells to perform computation
Processing-
Using-DRAM
…
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: In this work, we focus on processing-using-memory architectures. In particular, its implementation using DRAM.
Before I introduce processing-using-DRAM architectures, I will provide a short background on DRAM organization and operation.
[NEXT]

## Slide 7: Outline
Introduction
1
Background
2
PUD’s Limitations & Key Ideas
3
Proteus
4
Evaluation
5
Conclusion
6
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: [NEXT]

## Slide 8: Background: DRAM Hierarchical Organization (I)
local sense amplifier
local row decoder
bitline
wordline
DRAM subarray
(e.g., 65,536 rows)
DRAM mat
(e.g., 512 rows/columns)
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: DRAM chips are hierarchically organized.
[CLICK] On the bottom level, we have a DRAM mat, which is a 2D array of DRAM cells
[CLICK] Rows in a DRAM mat share a wordline,
[CLICK] and columns share a bitline
[CLICK] Columns are connected to a set of local sense amplifiers
[CLICK] and rows are connected to a local row decoder
[CLICK] Multiple DRAM mats constitute a DRAM subarray
[NEXT]

## Slide 9: Background: DRAM Hierarchical Organization (II)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: The many mats in a DRAM subarray are indexed using a global row decoder, which propagates the target row address across all mats using the global wordline
[CLICK] To move data outside a mat, a DRAM subarray uses a global sense amplifier,
[CLICK] and to move data outside a DRAM subarray, a DRAM chip uses the I/O logic interface
[NEXT]

## Slide 10: Background: DRAM Operation – Row Access (ACTIVATE)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
global wordline
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: To access data, the memory controller executes two main operations.
[CLICK] To access a DRAM row, the memory controller issues an ACTIVATE command to DRAM. On receiving an ACT, the global and local row decoder assess the wordline of the target row, connecting the DRAM cells to the bitlines
[CLICK] Then, the sense amplifier senses the perturbation caused in the bitline, amplifying and latching the data from the DRAM cells
[NEXT]

## Slide 11: Background: DRAM Operation – Column Access (READ)
row decoder
IO interface
64 bits
8 bits
global sense amplifier
column
to memory channel
global wordline
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Then, the memory controller issues a read command to read a column of data from the previously latched DRAM row.
[CLICK] The read command moves the target DRAM column from the local sense amplifiers to the global sense amplifier and finally to the memory channel via the I/O interface
[NEXT]

## Slide 12: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
← src
← dst
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: The operating principles of DRAM can be used to implement bulk-bitwise operations inside DRAM. For example, RowClone implements in-DRAM row copy operation by issuing back-to-back ACTIVATE commands to DRAM
[CLICK] The first activate copies the source row into the local sense amplifier
[NEXT]

## Slide 13: Background: In-DRAM Row Copy
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. "RowClone: Fast and Energy-Efficient In-DRAM Bulk Data Copy and Initialization," in MICRO, 2013
In-DRAM row copy is performed by issuing back-to-back ACTIVATES to the DRAM
← src
← dst
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: The second activate connects the destination row to the local sense amplifier.
[CLICK] which allows the previously-latched source row to be written back to the destination row.
[NEXT]

## Slide 14: Background: In-DRAM Majority Operation
← src3
← src2
← src1
row decoder
IO interface
64 bits
8 bits
global sense amplifier
Seshadri, Vivek, et al. " Ambit: In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology," in MICRO, 2017
In-DRAM majority is performed by simultaneously activating three DRAM rows
← src3
← src2
← src1
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 15: Background: Bulk Bitwise Arithmetic Operations (I)
← Cin
← B0
← A0
row decoder
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: In order to implement bulk bitwise arithmetic operations, the authors of SIMDRAM implements a three-step framework that maps a designed operation into a series of in-DRAM row copy and majority operations. I will illustrate such process using a ripple carry adder.
In order to add two arrays A and B with data values of 1-bit, SIMDRAM converts
[CLICK] an AND/OR/NOT-based rippled carry adder into
[CLICK] its equivalent MAJ/NOT-based circuit.
[NEXT]

## Slide 16: Background: Bulk Bitwise Arithmetic Operations (I)
← Cin
← B0
← A0
← Cout
row decoder
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Then it issues in-DRAM triple-row activations in order to realize the required MAJ/NOT operations, one majority gate at a gate.
[NEXT]

## Slide 17: Background: Bulk Bitwise Arithmetic Operations (I)
← Cin
← B0
← A0
← Sum0
← Cout
row decoder
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
A
Sum
MAJ
Cout
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: In the end, one DRAM row will hold the generated Sum and carry out bits for the 1-bit addition operation.

## Slide 18: Background: Bulk Bitwise Arithmetic Operations (II)
← Cin
← BN
← AN
← Cout
row decoder
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
repeat for N bits
← SumN
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: This processes is repeated for all individual N bits in the input data word
[NEXT]

## Slide 19: Background: Bulk Bitwise Arithmetic Operations (II)
Oliveira, Geraldo F., et al. ”SIMDRAM: An End-to-End Framework for Bit-Serial SIMD Computing in DRAM," in ASPLOS, 2021
← Cin
← BN
← AN
← Cout
row decoder
Bulk bitwise arithmetic can be performed by orchestrating in-DRAM row copy and majority operations
Sum
A
B
Cin
Cout
A
B
C
A
B
C
MAJ
A
B
C
0
MAJ
A
B
C
1
MAJ
B
Cin
MAJ
Sum
MAJ
Cout
A
repeat for N bits
← SumN
Processing-Using-DRAM architectures (e.g., SIMDRAM) are very-wide (e.g., 65,536 wide) bit-serial SIMD engines
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Thus, SIMDRAM transforms a DRAM chip into a very-wide bit-serial SIMD engine.
[NEXT]

## Slide 20: Background: PUD in Commodity Off-the-Shelf DRAM
Commodity off-the-shelf DRAM chips can perform bulk bitwise operations without hardware modifications
https://arxiv.org/pdf/2402.18736.pdf
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Similarly, Ambit implements majority operations in-DRAM by simultaneously activating three DRAM rows.
[CLICK] When three rows are activated, they simultaneously perpetuate the bitline based on the DRAM cell's content
[CLICK] this allows the local sense amplifiers to compute the majority of the values stored in the DRAM cells
[NEXT]

## Slide 21: Outline
Introduction
1
Background
2
PUD’s Limitations & Key Ideas
3
Proteus
4
Evaluation
5
Conclusion
6
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Next, let’s look at the limitations of such PUD architecture
[NEXT]

## Slide 22: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Processing-using-DRAM (PUD) architectures often use a bit-serial execution model, operating on each bit of a data word individually. However, naïvely applying this model introduces three key challenges.
[CLICK] First, PUD systems rely on static data representations, leading to costly operations over incidental narrow values with small dynamic ranges. This results in wasted energy and poor performance. We can mitigate this by reducing the bit-precision of PUD operations, focusing computation on consequential bits.
[CLICK] Second, while PUD systems employ throughput-oriented execution to hide high operation latency, they do not reduce the latency of individual in-DRAM operations. We propose mapping bits across multiple DRAM arrays to execute in parallel, hiding latency even for small data volumes. This also allow us to implement bit-parallel in-DRAM arithmetic operations.
[CLICK] Third, bit-serial arithmetic scales poorly with bit-precision, causing high-precision operations to significantly degrade performance. We address this by adopting alternative data representations, where arithmetic latency is independent of bit-precision.
I will briefly expand on each issue next.
[NEXT].

## Slide 23: Limitations of PUD Systems: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Staring with the rigid and static data representation of bit-serial PUD architectures
[NEXT]

## Slide 24: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
B
Sum
1
0
0
A
bit0
bit1
bit2
0
0
0
0
0
bit7
bit3
bit4
bit5
bit6
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: [CLICK] It’ is well known that many applications display what is called narrow values, which are data with small dynamic range stored in large data formats. For example, let’s assume you have a data element A storing ’4` in its three least-significant bits. However, the minimum standard data format available in high-level programming languages as C is eight bits. Thus, the remaining 5 most significant bits of such data element will be leading 0s.
[CLICK] When adding two values that display narrow values using a bit-serial execution model
[NEXT]

## Slide 25: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (I)
Narrow Values:
data with small dynamic range stored in large data formats
inconsequential bits → do not contribute to the output’s dynamic range
← Cin
← B7
← A7
row decoder
← Sum7
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
B
Sum
1
0
0
A
bit0
bit1
bit2
0
0
0
0
0
bit7
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: The leading zero values will not contribute to the dynamic range of the produced output.
[CLICK] Yet, such inconsequential bits will still be processed by the bit-serial engine, wasting memory cycles and energy.
[NEXT]

## Slide 26: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (II)
Application Analysis: quantify the amount required bit-precision in real applications
0
8
16
24
32
pca
2mm
3mm
cov
dg
fdtd
gmm
gs
bp
hw
km
x264
Required Bit-Precision
minimum number of bits required to represent input operands
largest bit-precision
smallest bit-precision
bit-precision distribution
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: In our work, we quantized the amount of narrow values present in real applications.
To do so, we profiled the required bit-precision of data arrays of loops in twelve real-world applications.
[CLICK] We define the required-bit precision such as the minimum number of bits required to represent input operands.
[CLICK] In our box plots, whiskers extend to the largest and smallest bit-precision
[NEXT]

## Slide 27: Limitations of Bit-Serial PUD Systems: Rigid and Static Data Representation (II)
Application Analysis: quantify the amount required bit-precision in real applications
0
8
16
24
32
pca
2mm
3mm
cov
dg
fdtd
gmm
gs
bp
hw
km
x264
Required Bit-Precision
Applications display a significant amount of narrow values → bit-precision can be reduced from 32 bits to 20 bits, on average
narrow values
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: [CLICK] We make the key observation that applications display a significant amount of narrow values, where the bit-precision can be reduced from 32 bits to 20 bits on average.
[NEXT]

## Slide 28: Opportunities for Bit-Serial PUD: Narrow Values for PUD Operations
0
0
0
0
0
1
0
0
Narrow Values:
data with small dynamic range stored in large data formats
0
0
0
0
0
0
1
0
0
0
0
0
0
1
1
0
+
inconsequential bits → dynamically identify and skip during computation
← Cin
← B2
← A2
row decoder
← Sum2
A
B
Sum
bit0
bit7
bit1
bit2
bit3
bit4
bit5
bit6
0
1
2
3
4
5
6
7
Bit-Precision
Latency
0
1
2
3
4
5
6
7
Bit-Precision
Energy
x
x
saved latency
saved energy
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: In order to solve this issue, we propose to dynamically identify and skip inconsequential bits in narrow values during bit-serial operation.
[CLICK] Doing so allows our PUD substrate to save DRAM cycles and energy during PUD operation
[NEXT]

## Slide 29: Opportunities for Bit-Serial PUD: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Next, we discuss issue caused by PUD’s throughput-oriented execution with low latency tolerance
[NEXT]

## Slide 30: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (I)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
PUD operations are inherently slow → need to operate on each bit serially to perform an operation with a data width > 1
Problem
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: We observe that PUD operations are inherently slow due to the need to operate on each bit of a data world serially.
[CLICK] This issue is further exacerbated by the inter-bit dependency present in bit-serial arithmetic operations
[NEXT]

## Slide 31: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
2 (2’b10)
2 (2’b10)
+
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
tmp
tmp
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: I will illustrate this issue by showcasing a two-bit PUD addition operation of two plus two.
PUD substrates store all data bits of the input data world vertically within a single DRAM subarray
[NEXT]

## Slide 32: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: During operation, the MAJ/NOT operations required to implement the PUD addition will be first performed over bits 0 of the data world
[NEXT]

## Slide 33: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
inter-bit
dependency
ACT
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: During this process, a carry from bit 0 will be generate and propagate to the input carry that will be used for bit 1
Note that Inter-bit dependency forces the serialization of PUD primitives when bits of a data word are placed within the same DRAM subarray
[NEXT]

## Slide 34: Limitations of Bit-Serial PUD Systems: Throughput-Oriented Execution (II)
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
bit 1
inter-bit
dependency
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
tmp
tmp
ACT
ACT
ACT
ACT
ACT
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Only after the inter-bit dependency is satisfied, the MAJ/NOT operations over bit 1 can be executed, one MAJ/NOT operation per-time in a serial manner.
[NEXT]

## Slide 35: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (I)
Leverage bit-level parallelism to execute independent PUD primitives concurrently across different DRAM subarrays
Key Idea
MAJ
B1
Cin
A1
Sum1
MAJ
Cout
MAJ
MAJ
B0
Cin
A0
Sum0
MAJ
Cout
MAJ
bit 0
bit 1
inter-bit
dependency
inter-bit
independency
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: To reduce the latency of PUD operations, we aim to leverage bit-level parallelism to execute independent PUD primitives concurrently across different DRAM subarrays.
In the bit-serial addition example, after the carry from bit 0 is propagate to bit 1, the yellow and red MAJ gates become bit-independent and can be executed concurrently.
[NEXT]

## Slide 36: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (II)
Proteus’ one-bit per-subarray data mapping → scatter bits across subarrays to expose bit-level parallelism
← B1
← A0
← A1
row decoder
← B0
← Cin1
← Cin0
← tmp
← Cout1
← Cout0
← Sum1
← Sum0
subarray0
all-bits per-subarray → forces serialization across bits
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
one-bit per-subarray → exposes bit-level parallelism
inter-subarray interconnect*
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Chang, Kevin K. et al. ”Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM," in HPCA, 2016
Notes: In order to exploit such key idea, Proteus implements a specialized data mapping called one-bit per-subarray, where bits of a data world are scattered across DRAM subarrays for parallel execution.
[CLICK] In this example, instead of storing all-bits of the input arrays in a single DRAM subarray,
[CLICK] Proteus stores in subarray 0 bits 0 and subarray 1 bits 1 of the input arrays A and B. Thus allowing both subarrays to operate concurrently over bit-independent values
[CLICK] Besides that, Proteus leverages a high-bandwidth inter-subarray interconnect that allows for data movement (required during carry propagation) between neighboring DRAM subarrays.
[NEXT]

## Slide 37: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (III)
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Let’s see how proteus exploit bit-level parallelism in our two-digit bit-serial addition
[NEXT]

## Slide 38: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (III)
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
inter-subarray interconnect
ACT
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: First, Proteus executes the carry generation MAJ gate for bit 0 in subarray 0
[NEXT]

## Slide 39: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (III)
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
ACT
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Next, Proteus uses the inter-subarray interconnect to copy the generated carry from subarray 0 to subarray 1.
[NEXT]

## Slide 40: Opportunities for Bit-Serial PUD: Latency Reduction with Subarray Parallelism (III)
inter-subarray interconnect
MAJ
B0
Cin
MAJ
A0
Sum0
MAJ
Cout
bit 0
tmp
← B0
← Cin0
← A0
row decoder
← tmp
← Count0
← Sum0
MAJ
B1
Cin
MAJ
A1
Sum1
MAJ
Cout
bit 1
tmp
← B1
← Cin1
← A1
row decoder
← tmp
← Count1
← Sum1
subarray0
subarray1
1
2
3
4
5
6
7
8
DRAM Cycle
DRAM Command
ACT
ACT
ACT
ACT
ACT
ACT
saved cycles
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Afterward, bit-independency is achieved, and the remaining MAJ operations across bits 0 and 1 can be concurrently executed in subarrays 0 and 1, respectively, hence reducing overall latency
[NEXT]

## Slide 41: Opportunities for Bit-Serial PUD: Overview
PUD systems suffer from three sources of inefficiency due to the naive use of a bit-serial execution model
1
Rigid and Static Data Representation
leading to a subpar performance in the presence of narrow values
opportunity 1: narrow values for PUD computation
2
Throughput-Oriented Execution with Low Latency Tolerance
failing to reduce the latency of a single PUD operation
opportunity 2: DRAM parallelism for latency-oriented execution
3
Scalability Challenges for High-Precision Operations
due to the linear/quadratically scaling nature of bit-serial algorithms
opportunity 3: alternative data representation for high-precision computation
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Finally, let’s look at the third issue caused by bit-serial execution, which is the scalability challenge for high-precision operations
[NEXT]

## Slide 42: Limitations of Bit-Serial PUD Systems: Scalability Challenges for High-Precision
8
16
32
N
Bit-Precision
Latency
…
8
16
32
N
Bit-Precision
Energy
bit 0
MAJ
bit 1
MAJ
bit N
MAJ
…
…
Linearly-Scaling PUD Operations (e.g., addition)
8
16
32
64
Bit-Precision
Latency
8
16
32
64
Bit-Precision
Energy
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
bit N
MAJ
bit 1
MAJ
bit 0
MAJ
…
Quadratically-Scaling PUD Operations (e.g., multiplication)
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Due to inter-bit dependency, bit-serial operations scales linearly for addition and subtraction operations
[CLICK] And quadratically for multiplication operation,
Resulting in high latencies as the bit-precision increases
[NEXT]

## Slide 43: Opportunities for Bit-Serial PUD: Alternative Data Representation for High-Precision
Use the redundant binary representation (RBR) for high-precision PUD operations
Key Idea
each bit position is represented by two bits that can take on a value ∈ {−1, 0, 1} <0, 1, 0, -1> = 0 x 23 + 1 x 22 + 0 x 21 + (-1) x 20 = 4 - 1 = 3
+
A0
B0
+
+
A1
B1
+
C0
C1
B2
+
A2
+
C2
BN
+
AN
+
CN
…
RBR-Based Arithmetic
limits carry propagation to at most two places
latency is independent bit-precision
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: To solve such an issue, we propose to use alternative data representation formats for high-precision PUD operations. In particular, we use the redundant binary representation format.
[CLICK] In such data format, each bit position is represented by two bits that can take a value of -1, 0, or 1. For example, the number 3 can be represented using for bits such as 0, 1, 0, and -1
[CLICK] Because of its redundancy nature, when implementing RBR-based arithmetic, the carry propagation is limited by at most two places, making the latency of PUD operations using such data format independent of the bit-precision
[NEXT]

## Slide 44: Outline
Introduction
1
Background
2
PUD’s Limitations & Key Ideas
3
Proteus
4
Evaluation
5
Conclusion
6
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Based on these key ideas, we propose Proteus
[NEXT]

## Slide 45: Proteus: Design Overview (I)
3
Program Select Unit
2
Dynamic Bit-Precision Engine
1
Parallelism-Aware Program Library
Proteus, a data-aware hardware runtime framework that dynamically and transparently adapts the in-DRAM implementation, bit-precision, and data format based on the input data for efficient PUD execution
  Proteus is composed of three main components:
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Proteus IS a data-aware runtime mechanism for efficient PUD execution. Proteus adapts the bit-precision, in-DRAM implementation, and data format based on the target input data transparently from the user.
[CLICK[ Proteus is composed of three main components implemented at the memory controller:
[CLICK] A parallelism-aware uProgram library
[CLICK] a Dynamic bit-precision engine
[CLICK] and a uprogram select unit
I briefly elaborate on each component next
[NEXT]

## Slide 46: Proteus: Design Overview (II)
data transposition unit
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
H |  |  |  | 
R |  |  |  | 
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
precision:
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine
3
Program Select Unit
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
parallelism-aware Programs
impl. #2
latency
#bits
impl. n
latency
#bits
AP
AAP
AAP
done
…
AP
AAP
AAP
done
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: First, the parallelism-aware uProgram is a collection of hand-optimized implementations of different PUD operations (called uPrograms). Each implementation has different trade-offs in terms of performance based on the target bit-precision
[NEXT]

## Slide 47: Proteus: Design Overview (III)
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
data transposition unit
parallelism-aware Programs
object tracker
…
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
latency
#bits
impl. #2
AP
AAP
AAP
done
latency
#bits
impl. n
AP
AAP
AAP
done
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
R |  |  |  | 
H |  |  |  | 
7
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
9
9
evicted cache line
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit
precision:
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Second, the dynamic bit-precision engine aims to identify the dynamic range of evicted cache lines belonging to the target PUD operation by scanning the data within evicted cache lines to identify the largest value within a PUD memory object
[NEXT]

## Slide 48: Proteus: Design Overview (IV)
latency
#bits
impl. #1
Progs.
cost model
AAP
AP
AAP
done
data transposition unit
parallelism-aware Programs
…
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
latency
#bits
impl. #2
AP
AAP
AAP
done
latency
#bits
impl. n
AP
AAP
AAP
done
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
R |  |  |  | 
H |  |  |  | 
bit-precision cal.
log2
ALU
target
precision
Program
select unit
>
>
>
>
>
>
>
sorting
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit identifies the appropriate bit-precision based on the input operations of the
target PUD operation
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
7
9
precision:
4 bits
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Third, the uProgram select unit aims to identify the appropriate bit-precision based on the previously identified largest values belonging to the memory addresses involved in the PUD operation

## Slide 49: Proteus: Design Overview (IV)
data transposition unit
A | 0 | 7 | 0 | 1
B | 1 | 9 | 8 | 3
dynamic
bit-precision
engine
transpose
Proteus control unit
C |  |  |  | 
F |  |  |  | 
Z |  |  |  | 
last-level cache
R |  |  |  | 
H |  |  |  | 
>
>
>
>
>
>
>
sorting
1
Parallelism-Aware Program Library
hand-optimized implementations of different PUD operations with different
performance vs. bit-precision trade-offs
  Proteus is composed of three main components:
2
Dynamic Bit-Precision Engine identifies the dynamic range of evicted cache lines belonging to
the target PUD operation
3
Program Select Unit identifies the appropriate bit-precision based on the input operations of the
target PUD operation
Progs.
AAP
AP
AAP
done
AP
AAP
AAP
done
latency
#bits
impl. #2
AP
AAP
AAP
done
object tracker
addr | size | bw | max. value
A | 8k | 8 | 
B | 8k | 8 | 
7
9
bit-precision cal.
log2
ALU
target
precision
AP
AAP
AAP
done
parallelism-aware Programs
Program
select unit
cost model
…
impl. #1
impl. n
latency
#bits
latency
#bits
precision:
4 bits
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Based on this calculated target bit-precision, the uProgram select unit probes the parallelism-aware uProgram library to identify what is the best in-DRAM realization of the target operation based on the target bit-precision
[NEXT]

## Slide 50: Proteus: More in the Paper & GitHub
Detailed hardware description
Implementation of bit-parallel PUD operations
Pareto analyses for PUD operations
Data format conversion procedure
System integration
Proteus for floating-point operations
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Due to time constraints, I refer you to the paper for more details on proteus implementation, including Detailed hardware description, Implementation of bit-parallel PUD operations
Pareto analyses for PUD operations
Data format conversion procedure
System integration
Proteus for floating-point operations

## Slide 51: Proteus: More in the Paper & GitHub
Detailed hardware description
Implementation of bit-parallel PUD operations
Pareto analyses for PUD operations
Data format conversion procedure
System integration
Proteus for floating-point operations
https://arxiv.org/abs/2501.17466
https://github.com/CMU-SAFARI/Proteus
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: For more details, please, check our paper
[NEXT]

## Slide 52: Outline
Introduction
1
Background
2
PUD’s Limitations & Key Ideas
3
Proteus
4
Evaluation
5
Conclusion
6
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Next, I will give an overview of our evaluation results
[NEXT]

## Slide 53: Evaluation: Methodology Overview
Evaluation Setup
  CPU: Intel Skylake CPU
  GPU: NVIDIA A100 GPU (with and without Tensor Cores)
  PUD: SIMDRAM [Oliveira+, 2021]
  https://github.com/CMU-SAFARI/Proteus
Workloads
  12 workloads from Polybench, Rodinia, Phoenix, and SPEC2017
  Linear algebra, data mining, video processing, machine learning
Metrics
  CPU-normalized performance per area
  Energy reduction (compared to baseline CPU)
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: We compared Proteus to a high-end CPU and GPU, and a SIMDRAM
In our analyses, we use 12 workloads from four benchmark suites
And we evaluated CPU-normalized performance per area and energy savings
[NEXT[

## Slide 54: Evaluation: Performance Analysis
Chart: CPU-Normalized Performance/mm2
| 2mm | 3mm | bp | cov | dg | fdtd | gmm | gs | hw | km | pca | x264 | GMean
GPU | 211.61 | 123.42 | 0.0024 | 82.55 | 96.77 | 2.27 | 3.67 | 2.32
SIMDRAM | 2.22 | 1.69 | 6955.88 | 283.58 | 0.2 | 0.04 | 0.84 | 5.69 | 0.05 | 0.77 | 0.06 | 0.62 | 1.66
Proteus (Only w/ Dynamic Bit-Precision) | 7.72 | 18.86 | 35014.76 | 335.85 | 2.25 | 4.46 | 2.84 | 46.64 | 0.16 | 2.49 | 0.94 | 1.99 | 10.43
Proteus | 14.61 | 26.43 | 54891.64 | 1360.9 | 2.83 | 5.05 | 5.37 | 64.61 | 0.28 | 11.75 | 1.07 | 3.06 | 16.98
Proteus significantly improves performance/mm2 compared to CPU (17x), GPU (7.3x), and SIMDRAM (10.2x)
Takeaway
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: First, in terms of
[CLICK] performance per area, compared to the CPU,
[CLICK] GPU
[CLICK] SIMDRAM, and
[CLICK] Proteus with only its dynamic bit-precision engine enabled
[CLICK] Proteus can
[CLICK] lead to significant performance improvements.
[CLICK] We observe that a significant portion of such improvements comes from our dynamic bit-precision engine.
[NEXT]

## Slide 55: Evaluation: Energy Analysis
Proteus significantly improves energy-efficiency compared to CPU (90.3x), GPU (21x), and SIMDRAM (8.1x)
Takeaway
Chart: CPU-Normalized Energy Reduction
| 2mm | 3mm | bp | cov | dg | fdtd | gmm | gs | hw | km | pca | x264 | Gmean
GPU | 133.666 | 137.751 | 0.004 | 62.848 | 163.015 | 0.001 | 9.166 | 14.832 | 4.279
SIMDRAM | 13.85 | 20.286 | 548.649 | 2941.47 | 2.992 | 0.566 | 10.539 | 13.359 | 0.713 | 9.869 | 1.279 | 3.633 | 11.108
Proteus (Only w/ Dynamic Bit-Precision) | 59.764 | 284.603 | 3426.534 | 4224.656 | 42.203 | 100.775 | 43.966 | 136.038 | 2.915 | 39.355 | 23.889 | 13.486 | 88.52
Proteus | 59.764 | 284.603 | 3426.534 | 11653.015 | 42.203 | 109.32 | 43.966 | 136.038 | 2.915 | 142.796 | 24.424 | 14.939 | 90.307
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Second, in terms of
[CLICK] energy savings, we compared to the CPU,
[CLICK] GPU
[CLICK] SIMDRAM, and
[CLICK] Proteus with only its dynamic bit-precision engine enabled
[CLICK] Proteus can
[CLICK] lead to significant energy-efficient improvements.
[NEXT]

## Slide 56: Evaluation: More in the Paper
Proteus with statically-identified narrow values
Data mapping and representation format conversion overheads
Performance of floating-point operations
Proteus versus Tensor Cores in GPUs
Area analysis
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: In our paper, we have further analysis including Proteus with statically-identified narrow values
Data mapping and representation format conversion overheads
Performance of floating-point operations
Proteus versus Tensor Cores in GPUs
Area analysis

## Slide 57: Evaluation: More in the Paper
Proteus with statically-identified narrow values
Data mapping and representation format conversion overheads
Performance of floating-point operations
Proteus versus Tensor Cores in GPUs
Area analysis
https://arxiv.org/abs/2501.17466
https://github.com/CMU-SAFARI/Proteus
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: For all that, please check our paper
[NEXT]

## Slide 58: Outline
Introduction
1
Background
2
PUD’s Limitations & Key Ideas
3
Proteus
4
Evaluation
5
Conclusion
6
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: Next, I will conclude this talk
[NEXT]

## Slide 59: Conclusion
https://github.com/CMU-SAFARI/Proteus
We introduce Proteus, a data-aware hardware runtime PUD framework that
that dynamically adjusts the bit-precision and chooses and uses the most appropriate data representation and arithmetic algorithm implementation for a given PUD operation
Our extensive evaluation shows that Proteus achieves
17x (90.3x), 7.3x (21x), and 10.2x (8.1x) the performance per mm2 (energy reduction) of a CPU, GPU, and state-of-the-art PUD system, small area cost to a DRAM chip (1.6%) and CPU die (0.03%)
Introduction | Background | PUD’s Limitations & Key Ideas | Proteus | Evaluation | Conclusion
● ● | ● ● ● ● ● ● ● ● | ● ● ● ● ● ● ● ● ● ● ● | ● ● ● ● ● | ● ● ● ● | ●
Notes: [CLICK] In this talk , we proposed Proteus, a a data-aware hardware runtime PUD framework that dynamically adjusts the bit-precision and based on that chooses and uses the most appropriate data representation and arithmetic algorithm implementation for a given PUD operation
[CLICK] We extensively evaluate Proteus and observe that it significantly improves performance and energy to processor-centric and memory-centric architectures while incurring small area overheads
[NEXT]

## Slide 60
Proteus Achieving High-Performance Processing-Using-DRAM with Dynamic Bit-Precision, Adaptive Data Representation, and Flexible Arithmetic
Geraldo F. Oliveira |  |  | 
Mayank Kabra | Yuxin Guo | Kangqi Chen | Giray Yağlıkçı
Melina Soysal | Mohammad Sadr | Joaquin O. Bueno | Saugata Ghose
Juan Gómez-Luna |  | Onur Mutlu | 
2025 International Conference on Supercomputing (ICS)
Notes: Thank you for your attention, I will be glad to take questions.

## Slide 61
Proteus Achieving High-Performance Processing-Using-DRAM with Dynamic Bit-Precision, Adaptive Data Representation, and Flexible Arithmetic
Geraldo F. Oliveira |  |  | 
Mayank Kabra | Yuxin Guo | Kangqi Chen | Giray Yağlıkçı
Melina Soysal | Mohammad Sadr | Joaquin O. Bueno | Saugata Ghose
Juan Gómez-Luna |  | Onur Mutlu | 
2025 International Conference on Supercomputing (ICS)
Backup Slides
Notes: Thank you for your attention, I will be glad to take questions.

## Slide 62: Cost Model Logic
We estimate, using CACTI [248], that the access
latency and energy per access of the 64 B SRAM array (used in our Cost Model Logic) is of 0.07 ns (i.e., less than 1 CPU cycle) and 0.000 04 nJ

## Slide 63: Pareto Analysis: Addition

## Slide 64: Pareto Analysis: Multiplication

## Slide 65: Calculating Bit-Precision

## Slide 66: Data Format Conversion

## Slide 67: Proteus for Floating-Point

## Slide 68: Evaluation System Configuration

## Slide 69: Evaluated Workloads

## Slide 70: Is Static Profiling Good Enough?
Proteus’ Dynamic Bit-Precision Engine further increases performance by 46%, over Proteus with static bit-precision. This happens because for statically profiled bit-precision, we must round the
bit-precision up to the nearest power-of-two.

## Slide 71: Data Conversion Overhead

## Slide 72: Proteus vs. Tensor Cores

## Slide 73: PUD and RowHammer