## Slide 1: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, PuDHammer [..]

## Slide 2: Executive Summary
Experimental Study: 316 COTS DDR4 chips from four major manufacturers to study read disturbance effects of multiple-row activation, which we call PuDHammer
PuDHammer significantly exacerbates DRAM read disturbance, causing up to 158.58x reduction in min. hammer count to induce first bitflip
PuDHammer bypasses in-DRAM RowHammer mitigation in DDR4 and induces 11340x more bitflips than RowHammer
Motivation: Processing-using-DRAM (PuD) alleviates data movement bottlenecks
DRAM can perform many PuD operations by activating multiple DRAM rows in quick succession or simultaneously (i.e., multiple-row activation)
Modern DRAM is subject to read disturbance (e.g., RowHammer)
    Repeatedly activating even a single row induces bitflips in unaccessed rows
Problem: No prior work studies the read disturbance effects of multiple-row activation
Goal: Understand and analyze read disturbance effects of multiple-row activation
Mitigation: We adapt Per Row Activation Counting (PRAC) for PuDHammer
Adapted PRAC solution incurs an average system performance overhead of 48.26%

## Slide 3: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 4: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 5: DRAM Organization
Row Decoder
DRAM Subarray
DRAM Module
DRAM
Chip
Bitline
DRAM Row
DRAM Cell
Wordline
Sense Amps.
DRAM Chip
…
…
Bank
Chip I/O
DRAM Bank
Subarray
Notes: DRAM is used as the main memory in many computing systems.
[CLICK] a DRAM module consists of multiple DRAM chips
[CLICK]Each chip contains multiple banks
[CLICK] Each bank is composed of multiple subarrays and sense amplifiers
[CLICK] And within each subarray, there is a two dimensional array of DRAM cells.
[CLICK] These cells are organized into rows that are selected using wordlines
[CLICK] And the cells are connected to a row of sense amplifiers via bitlines

## Slide 6: DRAM Operation
DRAM Subarray
Sense
Amplifiers
I/O Circuitry
ACTIVATE (ACT):
Fetch the row’s content into the sense amplifiers
Column Access (RD/WR): Read/Write the target column and drive to I/O
PRECHARGE (PRE): Prepare the bank for a new ACTIVATE
1
2
3
Notes: Data is internally accessed in a row granularity. To access data,
[CLICK] the memory controller first needs to activate the row that contains the data and fetch the row’s content into the sense amplifiers
[CLICK] Then, column accesses are serviced from the sense amplifiers
[CLICK] Finally, the subarray needs to be precharged to get ready for the next row activation

## Slide 7: Data Movement Bottleneck
Today’s computing systems are processor centric
All data is processed in the processor  at great system cost
Memory
Channel
Main Memory
(DRAM)
Computing Unit
(CPU, GPU, FPGA, Accelerators)
More than 60% of the total system energy is spent on data movement1
1 A. Boroumand et al., “Google Workloads for Consumer Devices: Mitigating Data Movement Bottlenecks,” ASPLOS, 2018
Notes: As we see until now, DRAM is just used to store data
[CLICK] As today’s computing systems are processor centric
[CLICK] All data needs to be processed in the processor
[CLICK] As a result, we need to move data very frequently
[CLICK] Prior work shows that more than 60% of the total energy is spent on this data movement

## Slide 8: Processing-using-DRAM (PuD)
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
DRAM Vault
Processing-using-DRAM uses the analog operational principles of DRAM cells to perform computation
Processing-
Using-DRAM
…
…
Multiple-row activation is a key technique to realize many PuD operations (e.g., AND and OR)
Notes: Processing-in-Memory architectures alleviate data movement bottlenecks using the analog operating principles of the memory cells to perform computation, in what is called processing-using-memory
Many PuD operations involves a key technique called multiple-row activation

## Slide 9: Processing-using-DRAM (PuD)
DRAM Bank
DRAM (e.g., 3D-Stacked Memory)
Vault
Controller
PHY
DRAM Vault
Processing-
Using-DRAM
…
…
Processing-
Using-DRAM
…
…
Multiple-row activation is a key technique to realize many PuD operations
1. Consecutive Multiple-Row Activation (CoMRA)
2. Simultaneous Multiple-Row Activation (SiMRA)
Multiple-row activation is a key technique to realize many PuD operations
Notes: We categorize multiple-row activation into two categories
First, consecutive multiple-row activation, CoMRA
Second, simultaneous multiple-row activatio,, SiMRA
Now, let me dive deeper into these two and give their key ideas

## Slide 10: Consecutive Multiple-Row Activation
Violating timing of PRE command greatly in COTS DRAM chips activates two rows consecutively
Notes: First, Consecutive Multiple-Row Activation.
[CLICK] The key observation is that violating timing of PRE command greatly can activate two rows consecutively

## Slide 11: Consecutive Multiple-Row Activation
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
s
t
d
d
s
t
s
r
c
Violating timing of PRE command greatly in COTS DRAM chips activates two rows consecutively
Notes: Let’s see how CoMRA works with an example: Here we have two rows source, src, and destination, dst.
[CLICK] If we obey the DRAM timing parameters while issuing this command sequence
[CLICK] We will only activate a single DRAM row at once, firstly source and then destination

## Slide 12: Consecutive Multiple-Row Activation
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
d
s
t
s
r
c
src’s content is copied to dst
s
r
c
Violating timing of PRE command greatly in COTS DRAM chips activates two rows consecutively
Notes: However, if we violate the timing between PRE and ACT dst
[CLICK] We can activate destination row without deactivating sense amplifier and keeping the bitlines at source voltage level
[CLICK] As a result of this, we can perform in-dram row copy operation: source row can be copied to destination row

## Slide 13: Simultaneous Multiple-Row Activation
Activating two rows in quick succession
in COTS DRAM chips simultaneously activates multiple rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Now let’s see how SiMRA works
[CLICK] The key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] In this pictorial example Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we can activate many rows at once in the same subarray

## Slide 14: Example: In-DRAM Majority-of-Three (MAJ3)
d
s
t
b
b
b
b
b
b
a
a
a
b
b
b
[Seshadri+ MICRO’17, Gao+ MICRO’19]
Assert three rows’ wordlines
Three rows perturb bitlines simultaneously
Sense amplifiers sample the output of majority
ACT
PRE
ACT
<3ns
<3ns
Notes: One example of SiMRA is In-DRAM MAJ3 operation
[CLICK] Assume ACT-PRE-ACT with violated timnigs will activate three rows simultaneously that contain a,b, and b values, respectively.
[CLICK] By activating three rows simultaneously, DRAM will assert these rows’ wordlines
[CLICK] After that these activated rows perturb bitlines simultaneously
[CLICK] After some time, sense amplifier amplifies the perturbation on the bitline and sample the output of majority of the values stored in activated rows, which is b in this example

## Slide 15: Read Disturbance in DRAM
Unfortunately, even activating a single DRAM row disturbs the data integrity of other unaccessed DRAM rows
Prominent example: RowHammer
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 2
closed
DRAM Subarray
Victim Row
Victim Row
Aggressor Row
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
[Kim+, ISCA’14]
Notes: Read disturbance bitflips have significant system-level implications because they break memory isolation.
[CLICK] Even activating a single DRAM row disturbs the data integrity of ther unaccessed DRAM rows.
[CLICK] A prominent example of read disturbance is RowHammer.
[CLICKx9] Repeatedly activating and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
We call the repeatedly activated row the aggressor row and the rows that have bitflips victim rows.

## Slide 16: Outline
Background
Testing Infrastructure
Combined Effect of CoMRA, SiMRA, and RowHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: This phenomenon brings us to the problem and the goal of this paper

## Slide 17: Problem & Goal
Problem
No prior work investigates the read disturbance effects of multiple-row activation
Goal
Understand how multiple-row activation affects read disturbance vulnerability in DRAM

## Slide 18: Outline
Background
Real DRAM Chip Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: To experiment with DRAM chips, we build a real DRAM chip testing infrastructure

## Slide 19: DRAM Bender: DRAM Testing Infrastructure
Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-based Infrastructure to Easily Test State-of-the-art DRAM Chips," TCAD, 2023.
Fine-grained control over DRAM commands, timings, temperature, and voltage
Notes: This infrastucture
[CLICK] enables fine-grained control over DRAM commands, timings, temperature and voltage
This picture shows one setup that contains one module and a host machine

## Slide 20: Laboratory for Understanding Memory
Notes: And in our lab, we have many machines to test many DRAM modules and chips

## Slide 21: DRAM Chips Tested
316 DDR4 chips from four major DRAM manufacturers
Covers different die revisions and chip densities
Notes: [CLICK] We test 316 DDR4 chips from four major DRAM manufacturers,
[CLICK] covering different die densities and revisions

## Slide 22: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Now, let’s move onto our first analysis

## Slide 23: Consecutive Multiple-Row Activation
d
s
t
r
c
s
36ns
ACT src
PRE
ACT dst
<9ns
14ns
d
s
t
s
r
c
src’s content is copied to dst
s
r
c
Violating timing of PRE command greatly in COTS DRAM chips activates two rows consecutively
Notes: Let’s recall that CoMRA violates PRE to ACT to activate two rows consecutively, which allows to perform in-DRAM row copy operation

## Slide 24: Hammering with CoMRA
DRAM Subarray
.
.
.
.
.
.
Double-Sided
Single-Sided
.
.
.
DRAM Subarray
src
dst
dst
src
ACT src
ACT dst
PRE
7.5ns
36ns
victim
victim
victim
victim
victim
aggressor
aggressor
aggressor
aggressor
Notes: To hammer using CoMRA access pattern, we use two versions of hammering:
[CLICK] First, double-sided where we sandwich a victim row
[CLICK] We adapt CoMRA to perform copy operation to sandwich a victim row for double-sided
[CLICK] Second, single-sided where a single aggressor row disturbs its neighboring victim rows
[CLICK] To perform single-sided CoMRA, we perform the copy operation between two rows that are far away from each other

## Slide 25: Characterization Methodology
Carefully sweep
    Row addresses: src and dst
    Timing parameters: Between PRE → ACT
    Data Pattern: 0x00, 0xFF, 0xAA, and 0x55
    Temperature (◦C): 50, 60, 70, and 80
ACT
ACT
ACT src
PRE
ACT dst
.
.
.
src
victim
dst
aggressor
aggressor
.
.
.
DRAM Subarray
DRAM Bank
Temperature
50 ◦C
80 ◦C
Notes: To characterize the read disturbance effects of CoMRA
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between prechrage to activate command
[CLICK] Data pattern
[CLICK] And temperature

## Slide 26: Read Disturbance Vulnerability Metric: HCfirst
The minimum hammer count required to induce the first bitflip
Lower is worse
Record bitflips in victim
Victim Row
Aggressor Row (src)
Aggressor Row (dst)
1 Hammer
ACT src
ACT dst
PRE
PRE
Notes: To evaluate the read disturbance vulnerability of DRAM chips, we use widely-adopted metric called Hcfirst
[CLICK] which is the minimum hammer count required to induce the first bitflip and lower the Hcfirst worse the read disturbance is
[CLICK] Here we have a double sided scenario where we sandwich a victim row
[CLICK] We count one CoMRa operation, ACT-PRE-ACT as 1 Hammer and we record bitflips in victim

## Slide 27: Double-Sided CoMRA vs. RowHammer (I)
13.98x
Double-sided CoMRA decreases lowest HCfirst by 13.98x compared to double-sided RowHammer
Lowest HCfirst reduction trend consistent across all four manufacturer
1.18x
3.28x
1.58x

## Slide 28: Double-Sided CoMRA vs. RowHammer (II)
Represents 99% of tested victim rows
Represents 50% of tested victim rows
HCfirst reduction of 50%
RowHammer HCfirst = 100
CoMRA HCfirst = 50
DRAM Rows (sorted by reducing HCfirst changes)
CoMRA reduces HCfirst
Notes: In this experiment,
[CLICK]
we investigate how much Hcfirst changes when we perform CoMRA compared to RowHammer
[CLICK] across all the tested DRAM rows sorted by reducing Hcfirst changes value on the x-axis.
[CLICK] Each curve in this plot represents a different DRAM vendor
Now let me walk through what this plot represents
[CLICK] X-axis from P1 to P100 shows 99% of the tested rows
[CLICK] Similarly, from P50 to P100 represents 50% of the tested rows
[CLICK] Hcfirst change of -50 means Hcfirst reduction of 50%
For example, a victim row has Hcfirst of 100 for RowHammer while having 50 for CoMRA

## Slide 29: Double-Sided CoMRA vs. RowHammer (II)
>99% of tested victim rows
experience lower HCfirst
Double-sided CoMRA decreases HCfirst for a large fraction of rows compared to double-sided RowHammer

## Slide 30: Double-Sided CoMRA vs. RowHammer
CoMRA exacerbates DRAM’s vulnerability to read disturbance in all four major manufacturers
Key Takeaway
HCFirst Compared to RH (%)

## Slide 31: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 32: Recall: SiMRA
Activating two rows in quick succession
in COTS DRAM chips simultaneously activates multiple rows in a subarray
36ns
ACT Row A
PRE
ACT Row B
<3ns
<3ns
14ns
Subarray X
Row A
Row B
DRAM Bank
…
ACT
ACT
Notes: Our key observation is activating two rows in quick succession can simultaneously activate many rows in a subarray
[CLICK] You may remember this pictorial example where Row A and Row B is in Subarray X.
[CLICK] When we respect to the timing parameters between ACT and PRE and PRE and ACT
[CLICK] we activate a single row at a time.
[CLICK] However, when we greatly violate these timing parameters, we observe that we can activate many rows at once in the same subarray

## Slide 33: Characterization Methodology
Carefully sweep
    Row addresses: Row A and Row B
    Timing parameters: Between ACT → PRE and PRE → ACT
    Data Pattern: 0x00, 0xFF, 0xAA, and 0x55
    Temperature (◦C): 50, 60, 70, and 80
Temperature
50 ◦C
80 ◦C
Subarray X
DRAM Bank
…
ACT
ACT
ACT Row A
PRE
ACT Row B
Row A
Row B
Notes: [CLICK] In this study, we focus on individual subarrays, here denoted as Subarray X
[CLICK] We perform our experiment using the following command sequence: Activate Row A, Precharge, and Activate Row B, where Row A and Row B in the same subarray
[CLICK] We carefully sweep four parameters: Row addresses: Row A and Row B
[CLICK] Timing parameters between ACT Row A and Precharge and between Precharge and ACT Row B

## Slide 34: Double-Sided SiMRA vs. RowHammer (I)
159x
Double-sided SiMRA decreases lowest HCfirst by 159x compared to double-sided RowHammer
51x
86x
125x
Lowest HCfirst reduction trend consistent across all tested number of simultaneously activated rows
Min. hammer count to induce first bitflip
#Simultaneously Activated Rows

## Slide 35: Double-Sided SiMRA vs. RowHammer (II)
>99% of tested victim rows
experience lower HCfirst
at least 25.19% of tested victim rows experience >99% HCfirst reduction

## Slide 36: Double-Sided SiMRA vs. RowHammer (II)
Double-sided SiMRA significantly decreases HCfirst for a majority of rows compared to double-sided RowHammer

## Slide 37: Double-sided SiMRA vs. RowHammer
SiMRA drastically exacerbates DRAM’s vulnerability to read disturbance
Key Takeaway

## Slide 38: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 39: Mitigating PuDHammer
2
Adapt RowHammer mitigations to account for PuDHammer
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 40: Mitigating PuDHammer
2
Adapt RowHammer mitigations to account for PuDHammer
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 41: Target Row Refresh (TRR)
Row 0
Row 1
Row 2
Row 3
Row 4
TRR-equipped DRAM Chip
TRR
Memory Controller
DRAM vendors equip their DRAM chips with a proprietary mitigation mechanisms known as Target Row Refresh (TRR)
Aggressor detected: Row 2
Refresh neighbor rows
TRR-induced refreshes
Key Idea: TRR refreshes nearby rows upon detecting an aggressor row
REF
aggressor
Notes: To protect their DRAM chips against RowHammer, DRAM vendors currently implement proprietary RowHammer mitigation mechanisms typically called Target Row Refresh or (TRR)
[CLICK] The key idea of TRR is to refresh nearby rows upon detecting an aggressor row
[CLICK] We demonstrate how TRR operates at a high-level.
[CLICK] The TRR mechanism detects [CLICK] an aggressor row as a result of [CLICK] repeatedly activating and precharging the same row. [CLICK]
[CLICK] To protect the neighbor victim rows from experiencing RowHammer bit flips, [CLICK] TRR refreshes the victim rows by performing TRR-induced refresh operations. TRR refreshes victim rows by piggybacking TRR-induced refreshes to the REFRESH commands that the memory controller periodically issues.

## Slide 42: Real DRAM Chip Results
>10K bitflips
<60 bitflips
>10K bitflips
~60 bitflips
CoMRA induces 1.10x more bitflips than RowHammer on average in the presence of TRR

## Slide 43: Real DRAM Chip Results
>10K bitflips
<60 bitflips
~240K bitflips
~180K bitflips
SiMRA induces 11340x more bitflips than RowHammer on average in the presence of TRR

## Slide 44: Mitigating PuDHammer
2
Adapt RowHammer mitigations to account for PuDHammer
Analyze the effectiveness of existing in-DRAM RowHammer mitigation against PuDHammer
1

## Slide 45: Adapting PRAC for PuDHammer
A Naïve Approach (PRAC-Naïve)
Reducing RowHammer threshold to SiMRA’s lowest observed HCfirst
Weighted Counting (PRAC-WC)
Increase counters based on the vulnerability caused by the operation (RH, CoMRA, and SiMRA)

## Slide 46: Methodology
Environment: Cycle-level DRAM simulator Ramulator2 [Kim+ CAL'15, Luo+ CAL'23]
System Configuration:
  Processor 4-core, out-of-order, 4.2GHz clock frequency
  DRAM DDR5, 1 channel, 2 rank/channel, 8 bank groups,
  4 banks/bank group, 128K rows/bank
  Memory Ctrl. 64-entry read and write requests queues,
  Scheduling policy: FR-FCFS with a column cap of 4
  PRAC 4 RFMs per Back-off
  PIM Unit 1-core, issues CoMRA & SiMRA operations with a fixed invertal
Workloads:
    60 five-core multiprogrammed workload mixes.
    Each mix is composed of
      four workloads from five major benchmark suites and
      one synthetic workload that periodically performs back-to-back one SiMRA with 32-row activation and one CoMRA operation

## Slide 47: Weighted Speedup Results
PRAC-Naïve
PRAC-WC
PRAC-Naïve
PRAC-WC
DRAM performs PuD operations in every 125ns
Normalized to no RH mitigation

## Slide 48: Weighted Speedup Results
PRAC-Naïve
PRAC-WC
PRAC-WC greatly outperforms PRAC-Naïve until 2us
PRAC-WC incurs an average (maximum) performance overhead of 48.26% (98.83%)

## Slide 49: More in the Paper
More characterization results
    Temperature, spatial variation, timing parameters, access pattern, data pattern, aggressor row on time analyses for CoMRA and SiMRA
    Combined Read Disturbance Effect of RowHammer with PuD
      Combined pattern is more effective than RowHammer alone (e.g., 1.66x reduction in HCfirst on average)
Details and analyses on mitigating PuDHammer
    Discussion on how modifying DRAM chips could help mitigating PuDHammer
    More details on PRAC adaptation
      Challenges on adapting for PuDHammer
      An area-efficient PRAC solution
      ..
Notes: We have more content in the paper, including
…

## Slide 50: Available on arXiv
https://arxiv.org/pdf/2506.12947
Notes: The extended version of our study is available on arxiv

## Slide 51: Outline
Background
Testing Infrastructure
Mitigating PuDHammer
Read Disturbance Effect of CoMRA
Conclusion
Read Disturbance Effect of SiMRA
Problem & Goal
Notes: Here is the outline of my talk

## Slide 52: Conclusion
We extensively study the interaction between read disturbance and multiple-row activation-based Processing-using-DRAM operations
We characterize 316 DDR4 chips from four major manufacturers
PuDHammer significantly exacerbates the read disturbance vulnerability (e.g., HCfirst reduces from 4K to 26)
PuDHammer bypasses in-DRAM RowHammer mitigation (TRR) and induces 11340x more bitflips than RowHammer
We hope our findings guide system-level and architectural solutions to enable read-disturbance-resilient future PuD systems
We adapt Per Row Activation Counting (PRAC) for PuDHammer
Incurs 48.26% performance overhead on average across 60 multiprogrammed workload mixes
Notes: In this study,
[CLICK] We experimentally demonstrate that off-the-shelf DRAM chips can simultaneously activate up to 32 DRAM rows
[CLICK] perform MAJ3, MAJ5, MAJ7, and MAJ9 operations
[CLICK] and copy one row’s content into up to 31 different rows simultaneously
[CLICK] We characterize the success rate of in-DRAM operations on 120 DDR4 chips from two major manufacturers And we highlight three key results
[CLICK] By storing multiple copies of majority’s input operands, we can increase the success rate of majority operations
[CLICK] and operating conditions can significantly affect the robustness of in-DRAM operations
[CLICK] We conclude that these empirical results demonstrate the promising potential of using DRAM as a computation substrate

## Slide 53: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 54: PuDHammer Experimental Analysis of Read Disturbance Effects of Processing-using-DRAM in Real DRAM Chips
İsmail Emir Yüksel
Akash Sood Ataberk Olgun Oğuzhan Canpolat Haocong Luo
Nisa Bostancı Mohammad Sadrosadati Giray Yağlıkçı Onur Mutlu
Backup Slides
Notes: Hello, I am Ismail Emir Yuksel.
I will be presenting our work, Simultaneous Many-Row Activation in Off-the-Shelf DRAM Chips

## Slide 55: CoMRA – Data Pattern
CheckerBoard pattern (i.e., 0x55/0xAA) is, in general, the most effective data pattern among the ones tested.

## Slide 56: CoMRA – Temperature
Read disturbance effects of hammering with double-sided CoMRA tend to get worse as temperature increases.

## Slide 57: Single-Sided CoMRA vs. RowHammer
Single-sided CoMRA decreases HCfirst compared to single-sided RowHammer
Single-sided CoMRA exhibits similar HCfirst distribution with far double-sided RowHammer.

## Slide 58: CoMRA (w/ increased tAggOn)
ACT src
ACT dst
PRE
7.5ns
36ns
36ns
Hammering with CoMRA
ACT src
ACT dst
PRE
7.5ns
36ns
tAggOn
(more than 36ns)
Pressing with CoMRA
PRE
PRE

## Slide 59: CoMRA (w/ Aggressor Row On Time) vs RowPress
For CoMRA
From 36ns to 70.2us
79x reduction
For RH/RP
From 36ns to 70.2us
31x reduction

## Slide 60: CoMRA (w/ Aggressor Row On Time) vs RowPress
Trend consistent across all four manufacturer:
Increasing tAggOn significantly reduces HCfirst for both CoMRA and RH/RP

## Slide 61: CoMRA (w/ Aggressor Row On Time) vs RowPress
Pressing with CoMRA is more effective than hammering with CoMRA
Key Takeaway 2

## Slide 62: CoMRA – Timing Delay
HCfirst increases as the latency of PRE→ACT dst increases

## Slide 63: CoMRA – Copy Direction
In most cases, copy direction has a small effect on HCfirst.

## Slide 64: CoMRA – Spatial Variation
HCfirst varies based on the victim row’s location in a subarray

## Slide 65: SiMRA Results

## Slide 66: SiMRA -- Impact of the Data Pattern
(Victim has negated data pattern)
Aggressor Rows = 0xFF..FF
Victim Rows = 0x00..00

## Slide 67: SiMRA -- Impact of the Data Pattern
(Victim has negated data pattern)
58x
Initializing victim rows with 0x00
increases avg. HCfirst by 58x
Dominant bitflip direction for SiMRA
1->0
Dominant bitflip direction for RH*
0->1
*not shown in the figure

## Slide 68: SiMRA -- Impact of the Data Pattern
Trend consistent across all tested number of simultaneously activated rows
SiMRA is significantly affected by data pattern and directionality of SiMRA and RowHammer bitflips are opposite
Key Takeaway

## Slide 69: SiMRA – Temperature
HCfirst decreases as temperature increases

## Slide 70: Single-Sided SiMRA vs. RowHammer
HCfirst consistently decreases as the number of simultaneously activated rows increases when performing single-sided SiMRA.

## Slide 71: SiMRA vs. RowPress
HCfirst decreases greatly as tAggOn increases

## Slide 72: SiMRA -- Timing Delay
HCfirst decreases greatly as tAggOn increases

## Slide 73: SiMRA – Spatial Variation
The effectiveness of SiMRA depends on the victim row’s location in a subarray.

## Slide 74: Combined PuDHammer, RH & RP

## Slide 75: Combined CoMRA & RH
DRAM rows experience significantly lower HCfirst when performing combined RowHammer and CoMRA.

## Slide 76: Combined SiMRA & RH
DRAM rows tend to experience lower HCfirst when performing combined RowHammer and SiMRA.

## Slide 77: Combined CoMRA, SiMRA & RH
Combined RowHammer with CoMRA & SiMRA together is the most effective combined access pattern to decrease HCfirst.

## Slide 78: Reverse Engineering TRR in Real DRAM
Key idea: Use data retention failures as a side channel
to detect when a row is refreshed by on-die mitigation
Notes: We use the methodology presented in this paper
[CLICK] Where the key idea is to use data retention failures as a side channel to detect when a row is refreshed by the on-die mitigation mechanism
[CLICK] We re-use the source code that is publicly available on this Github page.

## Slide 79: Per Row Activation Counting in DDR5 (April 2024)
DRAM Rows
0xA
PRAC Counters
DRAM Command Timeline
ACT A
ACT A
1
ACT A
ACT A
2
...
ACT A
ACT A
NBO
accurately tracks activation counts of each row
requires
preventive
action
Back-off
RFM
RFM
allocates a fixed time for preventive refresh
ACT
Back-off
continue to send commands
back-off threshold

## Slide 80: A Naïve Approach (PRAC-Naïve)
DRAM Rows
0xA
PRAC Counters
1
2
NBO
DRAM Command Timeline
ACT A
SiMRA
...
CoMRA
NBO=20
Lowest HCfirst for tested DRAM chips
RH: ~4K
CoMRA: ~400
SiMRA: ~20

## Slide 81: Weighted Counting (PRAC-WC)
DRAM Rows
0xA
PRAC Counters
1
201
NBO
DRAM Command Timeline
ACT A
SiMRA
...
CoMRA
NBO=4K
Threshold is set to 4K (RH Threshold) Each operation increases counters by
RH (ACT): 1
CoMRA: 10
SiMRA: 200

## Slide 82: Updating Multiple Counters in PRAC
SiMRA operation activates multiple rows simultaneously
    Which requires updating multiple PRAC row activation counters simultaneously
However, PRAC is designed to update only one counter upon an ACT command
    We need to modify the counter organization and operation in PRAC to support updating multiple counters.
Assuming we can activate up to N rows simultaneously
    Simultaneous access to N different counter values
    N incrementer circuits to update all the counters simultaneously

## Slide 83: A Solution: Chronus + N Incrementers
Time
ACT 0
PRE
ACT N
Row 0
Row N
Row 0
Counter 0
Counter 2N-1
Counter N+1
Counter N-1
Counter
Subarray
Row Decoder
Regular
Subarray
Row 2N-1
Row N
Row Decoder
Regular
Subarray
Row N-1
Row 0
Row Decoder
Row Buffer
Row Buffer
Row Buffer
Increment
Counter 0
Counter N-1
Row 0
Open Row
Row N
Serves
Regular
Accesses
Updates
Counter
Chronus concurrently updates counters while serving accesses

## Slide 84: Limitations of Tested COTS DRAM Chips
Some COTS DRAM chips do not support SiMRA
    We do not observe SiMRA in all tested Samsung/Micron chips
    Hypothesis
      Internal DRAM circuitry ignores the PRE command or the second ACT command when the timing parameters are greatly violated
    If such a limitation were not imposed, we believe these DRAM chips are also fundamentally capable of performing the operations we examine in this work

## Slide 85: In-DRAM Row-Copy (RowClone)
Fetch src’s content into the sense amplifiers
d
s
t
r
c
s
d
s
t
s
r
c
ACT src
Assert the src’s wordline
36ns
Notes: [CLICK] To perform RowClone, we first activate the source row by issuing ACT src command. This will assert the src’s wordline
[CLICK] and then fetch src’s content into the sense amplifiers

## Slide 86: In-DRAM Row-Copy (RowClone)
sense amplifier is still enabled
d
s
t
r
c
s
d
s
t
s
r
c
src’s content is copied to dst
s
r
c
ACT src
ACT dst
Bitlines are still at src voltage
PRE
7.5ns
36ns
Activates dst row
Notes: After that, we activate
[CLICK] the destination row without performing precharge operation in between two activate commands
[CLICK] By doing that DRAM will keep the bitlines at src voltage
[CLICK] and keep the sense amplifier enabled
[CLICK] As a result, after some time, the source row’s content is copied to the destination row

## Slide 87: Aggressor Row On Time & RowPress
Instead of using a high hammer count,
RowHammer
Aggressor Row
Open
Close
RowPress
Aggressor Row
Open
Close
☞ increase the time that the aggressor row stays open
[Luo+, ISCA’23]
hammer count = 2
Aggressor row on time (tAggON)
Minimum allowed row on time
(tRASmin)
Notes: In contrast, RowPress, instead of a high activation count, [CLICK] increases the time the that aggressor stays open.
Doing so disturbs adjacent rows enough to cause bitflips without having very high activation count.