## Slide 1: Improving Cache Performance by Exploiting Read-Write Disparity
Samira Khan, Alaa R. Alameldeen, Chris Wilkerson,
Onur Mutlu, and Daniel A. Jiménez

## Slide 2: Summary
  Read misses are more critical than write misses
    Read misses can stall processor, writes are not on the critical path
  Problem: Cache management does not exploit read-write disparity
  Goal: Design a cache that favors reads over writes to improve performance
    Lines that are only written to are less critical
    Prioritize lines that service read requests
  Key observation: Applications differ in their read reuse behavior in clean and dirty lines
  Idea: Read-Write Partitioning
    Dynamically partition the cache between clean and dirty lines
    Protect the partition that has more read hits
  Improves performance over three recent mechanisms
Notes: It has been widely known that read misses are more critical than the write misses. Read misses can stall the processor, where writes can be buffered and are not on the critical path. Unfortunately, our current cache management techniques do not exploit this disparity between read and write requests. Our goal in this work is to design a cache that favors read requests over write requests to maximize the number of read hits. We argue that lines that serves read requests should be protected in the cache, may be at the expense of the lines that service only write requests.
In order to design such a cache, we exploit the observation that applications differ in their read reuse in clean dirty lines. We propose a simple mechanism, read-write partitioning, which dynamically partitions the cache in clean and dirty lines and protect the partition the has more read hits.

## Slide 3: Outline
Motivation
Reuse Behavior of Dirty Lines
Read-Write Partitioning
Results
Conclusion
Notes: Here is the outline of the talk. First I will talk about the motivation behind the work and show that how exploiting the difference between read and write requests can improve performance. Then I will show that not all dirty lines are the same and talk about the read reuse behavior in dirty lines. Next I will explain the mechanism we propose to exploit disparity between reads and writes. Finally I will show the results and conclude with a summary.

## Slide 4: Motivation
time
STALL
STALL
Rd A
Wr B
Rd C
Buffer/writeback B
  Cache management does not exploit
  the disparity between read-write requests
  Read and write misses are not equally critical
  Read misses are more critical than write misses
    Read misses can stall the processor
    Writes are not on the critical path
Notes: As I have already mentioned, read and write requests are not equally critical. If there are no independent instructions to execute, a read miss can stall the processor.
Here I have a very simple figure to show this visually. A miss at read A stalls the processor. Where writes are buffered and usually are not on the critical path. So miss at Wr B does not stall the processor. Rd C again stalls the processor and so on.
Though the read and write requests are treated differently in the processor pipeline, cache management techniques do not exploit this disparity between read and write requests.

## Slide 5: Key Idea
Rd A
Wr B
Rd B
Wr C
Rd D
  Favor reads over writes in cache
  Differentiate between read vs. only written to lines
  Cache should protect lines that serve read requests
    Lines that are only written to are less critical
  Improve performance by maximizing read hits
  An Example
D
B
C
A
Read-Only
Read and Written
Write-Only
Notes: In this work, we propose that caches should be designed to favor read requests over write requests. In order to that we have to differentiate between lines that are read vs lines that are not read. We argue that caches should protect lines that service read misses, and can evict less critical lines that are only written to. This can lead to performance improvement by maximizing read hits.
[DO I MENTION THE DIFFERENCE BETWEEN REF VS NON REF?]
Let’s see an example that shows how this idea can improve the performance. Here we have a loop, that touches four cache lines, A, B, C and D. A and D are read only lines, where B is both read and written and C is only written to.

## Slide 6: An Example
C
B
D
Rd A M
STALL
WR B M
Rd B H
Wr C M
Rd D M
STALL
D
C
A
A
D
B
A
D
B
B
A
C
C
B
D
B
A
D
Rd A H
Wr B H
Rd B H
WR C M
Rd D M
STALL
D
B
A
A
D
B
B
A
C
B
A
D
A
D
B
Write B
Write C
LRU Replacement Policy
Write C
Write B
Read-Biased Replacement Policy
Replace C
Rd A
Wr B
Rd B
Wr C
Rd D
2 stalls per iteration
1 stall per iteration
Evicting lines that are only written to
can improve performance
cycles
saved
Dirty lines are treated differently
depending on read requests
Notes: First let’s see what happens in the LRU replacement policy. Suppose we have a cache that can hold only three lines. Since the loop touches four block, it thrashes the cache. In a stable iteration, Load A causes a miss, as the last access in the previous iteration replaced A. and it stalls the processor. The next access to B is also a miss, but does not cause a stall as the write gets buffered. Next we access B again and since it is already in the cache, it is a hit. Next access to C also causes a miss, but not one the critical path. Last access is to D, load D is also a miss, as it got evicted by C. So there are two stalls per iteration for this policy.
Now let’s see what happens in a read-biased policy. Since A, B, and D service read requests, this policy tries to protect these three lines. In a stable iteration, first access to A becomes a hit, as it is protected in the previous iteration. Accesses to B, and C becomes a hit. When we access D, We encounter a miss, and instead of replacing the LRU block, we replace C, as it does not service any read requests. So by protecting A we eliminate a miss. Read-biased policy has 1 stall per iteration where LRU have 2 stalls per iteration. So evicting write-only lines can improve performance.
So there is only one stall per iteration in this case.
The intersting thing here is, we cannot just evict dirty lines. Both B and C are dirty lines, but B is protected because it is read, where C is not protected as it is only written to. A no-write allocate policy would not diffrentiate between them and will bypass both B and C, but this will result in a miss when B is read. So we argue that we cannot treat all the dirty lines in the same way.

## Slide 7: Outline
Motivation
Reuse Behavior of Dirty Lines
Read-Write Partitioning
Results
Conclusion
Notes: This leads to our next topic that dirty lines have different behavior depending on

## Slide 8: Reuse Behavior of Dirty Lines
  Not all dirty lines are the same
  Write-only Lines
    Do not receive read requests, can be evicted
  Read-Write Lines
    Receive read requests, should be kept in the cache
Evicting write-only lines provides more space
for read lines and can improve performance
Notes: So the point we want to make is, not all dirty lines are the same. We categorize dirty lines into groups. Write-only lines do not serve any read requests, so they can be evicted, while read-write lines receive read requests, and should be protected in the cache. So now the question is, how many blocks are read-written and how many are only written to?

## Slide 9: Reuse Behavior of Dirty Lines
Chart: Percentage of Cachelines in LLC
| 400.perlbench | 401.bzip2 | 403.gcc | 410.bwaves | 429.mcf | 433.milc | 434.zeusmp | 435.gromacs | 436.cactusADM | 437.leslie3d | 445.gobmk | 447.dealII | 450.soplex | 456.hmmer | 458.sjeng | 459.GemsFDTD | 462.libquantum | 464.h264ref | 465.tonto | 470.lbm | 471.omnetpp | 473.astar | 481.wrf | 482.sphinx3 | 483.xalancbmk
Dirty (read-write) | 3.1037 | 54.2074 | 9.85 | 0 | 1.4209 | 0.07347 | 0.63798 | 30.8908 | 9e-05 | 0.35784 | 1.9841 | 40 | 10.2571 | 2.6878 | 4.1654 | 0.30349 | 0 | 0 | 16.6667 | 0.00014 | 15.0647 | 43.1102 | 0.74441 | 1.3146 | 0.38374
Dirty (write-only) | 10.6913 | 15.9344 | 2.3616 | 100 | 77.0494 | 37.131 | 37.5536 | 33.785 | 81.0226 | 28.5624 | 57.5397 | 20 | 19.6922 | 92.28 | 76.3483 | 46.8645 | 20.0064 | 7.1428 | 22.2222 | 65.2835 | 20.2532 | 19.6005 | 38.6285 | 3.303 | 1.8888
On average 37.4% lines are write-only,
9.4% lines are both read and written
Applications have different read reuse behavior
in dirty lines
Notes: Here we show the percentage of cache lines in LLC, that are both read and written vs that are only written to. in the x axis, we have spec cpu benchmarks, and in the y axis we have the percentage of cachelines in LLC. The first take-away from the graph is there is significant portion of lines that are only written to. On average, 37% blocks are written to, where 9% of the lines are read and written. The second take away from this graph is applications differ in their read reuse in dirty lines. For example, xalanc has very few dirty lines, where most of them are written to. Hmmer has a significant number of write-only lies, where soplex has good mix of write-only and read-write lines.

## Slide 10: Outline
Motivation
Reuse Behavior of Dirty Lines
Read-Write Partitioning
Results
Conclusion
Notes: We exploit this difference in read reuse behavior of dirty lines in our mechanism Read write partitioning.

## Slide 11: Read-Write Partitioning
Goal: Exploit different read reuse behavior in dirty lines to maximize number of read hits
Observation:
  Some applications have more reads to clean lines
  Other applications have more reads to dirty lines
Read-Write Partitioning:
  Dynamically partitions the cache in clean and dirty lines
  Evict lines from the partition that has less read reuse
Improves performance by protecting lines
with more read reuse

## Slide 12: Read-Write Partitioning
Applications have significantly different
read reuse behavior in clean and dirty lines
Chart: Soplex
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0
Clean Line | 0 | 1 | 1.82 | 2.4072 | 3.1592 | 3.7727
Dirty Line | 0 | 2.4193 | 4.1837 | 5.8176 | 7.5321 | 9.1082
Chart: Xalanc
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0
Clean Line | 0 | 1 | 1.7164 | 2.4249 | 3.0829 | 3.7831
Dirty Line | 0 | 0.022977 | 0.04159 | 0.059799 | 0.078492 | 0.099172
Notes: Here we show the number of reads in clean in dirty lines in two applications. We have soplex in the left side and xalan in the right side. In the x-axis we have number of instructions and in the y axis we have the number of reads normalized to number of reads at clean lines at 100 m instructions. Each point in the chart represents the cumulative number of hits at every 100 millions instructions.
We can see that for soplex there are significant number of reads at clean line, but there are almost 4X more hits in dirty lines. On the other hand, xalanc has insignificant number of reads in dirty lines, almost all the reads are being serviced by clean lines.

## Slide 13: Read-Write Partitioning
Utilize disparity in read reuse in clean and dirty lines
Partition the cache into clean and dirty lines
Predict the partition size that maximizes read hits
Maintain the partition through replacement
  DIP [Qureshi et al. 2007] selects victim within the partition
Cache Sets
Dirty Lines
Clean Lines
Predicted Best Partition Size 3
Replace from dirty partition

## Slide 14: Predicting Partition Size
Predicts partition size using sampled shadow tags
  Based on utility-based partitioning [Qureshi et al. 2006]
Counts the number of read hits in clean and dirty lines
Picks the partition (x, associativity – x) that maximizes number of read hits
P
E
D
E
L
M
A
S
S
S
T
T
E
R
S
C
O
U
N
T
E
R
S
C
O
U
N
S
H
A
D
O
W
S
H
A
D
O
W
T
A
G
S
T
A
G
S
MRU
MRU-1
LRU
LRU+1
…
MRU
MRU-1
LRU
LRU+1
…
Dirty
Clean
Maximum number of read hits
Notes: So how do we predict the partition size? We predict the best partition size using sampled shadow tags . Our mechanism is very similar to utility-based partitioning, But instead of determining the partition size among cores, we determine the partition size for clean and dirty lines. Each sampled set in the cache is associated with two shadow tag directories, one for clean lines and one for dirty lines. We count the number of read hits in shadow tags. We pick the partition that maximizes the number of read hits.

## Slide 15: Outline
Motivation
Reuse Behavior of Dirty Lines
Read-Write Partitioning
Results
Conclusion
Notes: Now that I have explained our mechanism, I will talk about the results.

## Slide 16: Methodology
CMP$im x86 cycle-accurate simulator [Jaleel et al. 2008]
4MB 16-way set-associative LLC
32KB I+D L1, 256KB L2
200-cycle DRAM access time
  550m representative instructions
Benchmarks:
  10 memory-intensive SPEC benchmarks
  35 multi-programmed applications

## Slide 17: Comparison Points
DIP, RRIP: Insertion Policy [Qureshi et al. 2007, Jaleel et al. 2010]
  Avoid thrashing and cache pollution
    Dynamically insert lines at different stack positions
  Low overhead
  Do not differentiate between read-write accesses
SUP+: Single-Use Reference Predictor [Piquet et al. 2007]
  Avoids cache pollution
    Bypasses lines that do not receive re-references
  High accuracy
  Does not differentiate between read-write accesses
    Does not bypass write-only lines
  High storage overhead, needs PC in LLC

## Slide 18: Comparison Points: Read Reference Predictor (RRP)
A new predictor inspired by prior works [Tyson et al. 1995, Piquet et al. 2007]
Identifies read and write-only lines by allocating PC
  Bypasses write-only lines
Writebacks are not associated with any PC
PC P: Rd A
Wb A
Wb A
Wb A
Wb A
Wb A
Marks P as a PC that allocates a line that is never read again
Associates the allocating PC in L1 and passes PC in L2, LLC
High storage overhead
PC Q: Wb A
No allocating PC
Allocating PC from L1
Time
Notes: We also compare our work with a new PC-based predictor proposed in this work called read reference predictor. It can identify read lines and write only lines using the allocating pc. Unlike previous work, it can also bypasses write-only lines. For example, if if a lines is allocated by PC P, then receives only write requests after that, we mark P as a PC that allocates line which is never read again. Next time, we see a line brought by PC P, RRP decides to bypass that line. However, one challenge with this predictor is that writeback requests are not associated with any PC. We associate the allocating PC at L1 with the writeback requests and pass that information in L2 and L3. This RRP predictor is very complex and requires high overhead.

## Slide 19: Single Core Performance
Differentiating read vs. write-only lines
improves performance over recent mechanisms
Chart: Speedup vs. Baseline LRU
| DIP | RRIP | SUP+ | RRP | RWP
 | 1.099 | 1.102 | 1.126 | 1.176 | 1.1461
+8%
+4.6%
-3.4%
2.6KB
48.4KB
RWP performs within 3.4% of RRP,
But requires 18X less storage overhead

## Slide 20: 4 Core Performance
Differentiating read vs. write-only lines
improves performance over recent mechanisms
Chart: Speedup vs. Baseline LRU
| No Memory Intensive | 1 Memory Intensive | 2 Memory Intensive | 3 Memory Intensive | 4 Memory Intensive
DIP | 1.0142 | 1.0347 | 1.0462 | 1.0201 | 1.0703
RRIP | 1.0303 | 1.0295 | 1.0416 | 1.0537 | 1.0729
SUP+ | 1.01 | 1.0305 | 1.0162 | 1.0113 | 1.0238
RRP | 1.0601 | 1.0781 | 1.0924 | 1.0797 | 1.1232
RWP | 1.0452 | 1.0507 | 1.0576 | 1.0661 | 1.0792
+4.5%
+8%
More benefit when more applications
are memory intensive

## Slide 21: Average Memory Traffic
Chart: Percentage of Memory Traffic
| Base | RWP
Miss | 85.07 | 66.29
Writeback | 14.92 | 17.42
Increases writeback traffic by 2.5%,
but reduces overall memory traffic by 16%

## Slide 22: Dirty Partition Sizes
Chart: Number of Cachelines
| 400.perlbench | 401.bzip2 | 403.gcc | 410.bwaves | 416.gamess | 429.mcf | 433.milc | 434.zeusmp | 435.gromacs | 436.cactusADM | 437.leslie3d | 444.namd | 445.gobmk | 447.dealII | 450.soplex | 453.povray | 454.calculix | 456.hmmer | 458.sjeng | 459.GemsFDTD | 462.libquantum | 464.h264ref | 465.tonto | 470.lbm | 471.omnetpp | 473.astar | 481.wrf | 482.sphinx3 | 483.xalancbmk
Natural Dirty Partition | 2.479 | 14.2 | 3.1619 | 9.9856 | 0.13745 | 6.0601 | 12.502 | 4.8625 | 10.8289 | 8.001 | 4.1023 | 1.7344 | 6.7629 | 2.428 | 6.9917 | 0.4 | 0.08 | 14 | 13.1 | 0.1521 | 0.0012207 | 6.1 | 8.6272 | 12.17 | 7.0928 | 9.6196 | 5.4199 | 1.12 | 0.94
Predicted Dirty Partition | 2 | 14 | 1 | 9 | 0 | 12 | 13 | 15 | 8 | 1 | 2 | 2 | 5 | 1 | 14 | 0 | 0 | 16 | 13 | 1 | 15 | 6 | 9 | 1 | 7 | 6 | 8 | 1 | 0
Partition size varies significantly
for some benchmarks

## Slide 23: Dirty Partition Sizes
Chart: Number of Cachelines
| 400.perlbench | 401.bzip2 | 403.gcc | 410.bwaves | 416.gamess | 429.mcf | 433.milc | 434.zeusmp | 435.gromacs | 436.cactusADM | 437.leslie3d | 444.namd | 445.gobmk | 447.dealII | 450.soplex | 453.povray | 454.calculix | 456.hmmer | 458.sjeng | 459.GemsFDTD | 462.libquantum | 464.h264ref | 465.tonto | 470.lbm | 471.omnetpp | 473.astar | 481.wrf | 482.sphinx3 | 483.xalancbmk
Natural Dirty Partition | 2.479 | 14.2 | 3.1619 | 9.9856 | 0.13745 | 6.0601 | 12.502 | 4.8625 | 10.8289 | 8.001 | 4.1023 | 1.7344 | 6.7629 | 2.428 | 6.9917 | 0.4 | 0.08 | 14 | 13.1 | 0.1521 | 0.0012207 | 6.1 | 8.6272 | 12.17 | 7.0928 | 9.6196 | 5.4199 | 1.12 | 0.94
Predicted Dirty Partition | 2 | 14 | 1 | 9 | 0 | 12 | 13 | 15 | 8 | 1 | 2 | 2 | 5 | 1 | 14 | 0 | 0 | 16 | 13 | 1 | 15 | 6 | 9 | 1 | 7 | 6 | 8 | 1 | 0
Partition size varies significantly during the runtime
for some benchmarks

## Slide 24: Outline
Motivation
Reuse Behavior of Dirty Lines
Read-Write Partitioning
Results
Conclusion
Notes: Now that I have shown the results, I will conclude with a summary.

## Slide 25: Conclusion
Problem: Cache management does not exploit read-write disparity
  Goal: Design a cache that favors read requests over write requests to improve performance
  Lines that are only written to are less critical
  Protect lines that serve read requests
Key observation: Applications differ in their read reuse behavior in clean and dirty lines
Idea: Read-Write Partitioning
  Dynamically partition the cache in clean and dirty lines
  Protect the partition that has more read hits
Results: Improves performance over three recent mechanisms

## Slide 26
Thank you

## Slide 27: Improving Cache Performance by Exploiting Read-Write Disparity
Samira Khan, Alaa R. Alameldeen, Chris Wilkerson,
Onur Mutlu, and Daniel A. Jiménez

## Slide 28: Extra Slides

## Slide 29: Reuse Behavior of Dirty Lines in LLC
  Different read reuse behavior in dirty lines
    Read Intensive/Non-Write Intensive
      Most accesses are reads, only a few writes
      Example: 483.xalancbmk
    Write Intensive
      Generates huge amount of intermediate data
      Example: 456.hmmer
    Read-Write Intensive
      Iteratively reads and writes huge amount of data
      Example: 450.soplex
Notes: Depending on the number of read reuse, we divide the applications, in three categories. Read intensive, write intensive and read-write intensive.

## Slide 30: Read Intensive/Non-Write Intensive
Most accesses are reads, only a few writes
483.xalancbmk: Extensible stylesheet language transformations (XSLT) processor
XML Input
HTML/XML/TXT Output
XSLT Code
XSLT Processor
92% accesses are reads
99% write accesses are stack operation
Notes: Let’s talk about the read intensive applications. In these applications, most of the accesses are reads, with only a few writes. One good example of this kind of workload is xalanc. It is a language transformation processor, which takes a XML file as an inout, uses the language transformation code to transform it to a html, text or another kind of XLM file. In our simulation at simpoint, 92% accesses are reads, and only 8% accesses are writes. And 99% of these writes are coming from stack operations.

## Slide 31: Non-Write Intensive
%ebp
%esi
elementAt
push %ebp
mov %esp, %ebp
push %esi
pop %esi
pop %ebp
ret
…
Logical View of Stack
WRITE
WRITE
WRITE
WRITE
READ
READ
READ
READ
WRITEBACK
WRITEBACK
Core Cache
Last Level Cache
Read and Written
Write-Only
1.8% lines in LLC are write-only
These dirty lines should be evicted
Notes: So let’s see how this is impacting the dirty lines in LLC. In the right side I have a function elementAt that frequently generates a large number of writes. As the name suggests, It returns a value at a specific position. In middle I show the logical view of the stack and in the left we have the core cache along with the last level cache. So this function first pushes some variables in the stack, which writes line in the core cache. When these variables are popped out of the stacked, the lines are read back. Since stack variables have short temporal locality, eventually these lines are written back to LLC, and they are evicted without being reused by any read requests. In our experiment, only 1.8% of the cache lines in LLC are write-only, and only 0.38% are read and written. So these are the benchmarks where read reuses mostly come from clean lines in LLC.

## Slide 32: Write Intensive
  Generates huge amount of intermediate data
456.hmmer: Searches a protein sequence database
Hidden Markov Model
of Multiple Sequence
Alignments
Best Ranked
Matches
Viterbi algorithm, uses dynamic programming
Only 0.4% writes are from stack operations
Database
Notes: The next group is the write intensive workloads. These applications generate a huge amount of intermediate data. One example of this kind of application is hammer, which searches a protein or gene sequence database. As input, it takes hidden markov model of multiple Sequence alignments and tries to find the best ranked matches from the database. You can think of searching with two somewhat similar proteins to figure out which other protein both of them can be derived from by some sequence of insertion, and deletions [IS THIS THE RIGHT WORD? ASK HONGYI]. This benchmark uses viterbi algorithm which is a dynamic programming algorithm. Inlike xalanc, only 0.4% writes come from the stack, so most of the writes are coming from allocated memory in the head.

## Slide 33: Write Intensive
92% lines in LLC are write-only
These lines can be evicted
WRITEBACK
WRITEBACK
Core Cache
Last Level Cache
READ/WRITE
2D Table
Write-Only
Read and Written
Notes: Like any other DP algorithm, it has 2D table, and each cell in the table gets calculated by operating on some cells in the previous row, but instead of one table, it operates on multiple table. So the cache lines in LLC gets read and written as the DP algorithm moves through a row. At some point, these lines are written back in to LLC. However, since the algorithm operates only on neighboring cells, these lines are not read back from the LLC. So LLC mostly stores write-only lines. In our experiment, 92% lines in LLC are write-only lines, where 2.68% lines are read and written.

## Slide 34: Read-Write Intensive
  Iteratively reads and writes huge amount of data
450.soplex: Linear programming solver
Inequalities and
objective function
Miminum/maximum
of objective function
Simplex algorithm, iterates over a matrix
Different operations over the entire matrix at each iteration
Notes: The third category that we have is read and write intensive applications. These applications iteratively reads and writes a huge amount of data. For example, soplex is an example for this kind of application. It is liner programming solver, which takes input a set of inequalities and an objective function, and tries to minimize or maximize that objective function.
The particular algorithm it employs is called simplex, which iterates over a matrix and performs different kind of operation on the whole matrix at each iteration.

## Slide 35: Read-Write Intensive
19% lines in LLC write-only, 10% lines are read-written
Read and written lines should be protected
WRITEBACK
Core Cache
Last Level Cache
READ
READ/WRITE
Pivot Column
Pivot Row
Read and Written
Read and Written
Write-Only
Notes: Let’s see what happens in the caches for soplex. So this the matrix and at first the algorithm selects a pivot column and a pivot row. And then it iterates through the whole matrix doing addition and multiplications on the rows. While doing so, it reads and writes lines in the core cache and writebacks some of the lines in LLC. However, then it starts a new iteration and again selects a pivot row and pivot column. And starts iterating though the whole matrix again. Therefore, lines written back to the LLC, gets read again. This is why soplex has reads in the LLC. 10% of the lines in the LLC are read and written and these lines should be protected to increases in read reuse.

## Slide 36: Read Reuse of Clean-Dirty Lines in LLC
Chart: Percentage of Cachelines in LLC
| 400.perlbench | 401.bzip2 | 403.gcc | 410.bwaves | 429.mcf | 433.milc | 434.zeusmp | 435.gromacs | 436.cactusADM | 437.leslie3d | 445.gobmk | 447.dealII | 450.soplex | 456.hmmer | 458.sjeng | 459.GemsFDTD | 462.libquantum | 464.h264ref | 465.tonto | 470.lbm | 471.omnetpp | 473.astar | 481.wrf | 482.sphinx3 | 483.xalancbmk
Dirty Read | 3.1037 | 54.2074 | 9.85 | 0 | 1.4209 | 0.07347 | 0.63798 | 30.8908 | 9e-05 | 0.35784 | 1.9841 | 40 | 10.2571 | 2.6878 | 4.1654 | 0.30349 | 0 | 0 | 16.6667 | 0.00014 | 15.0647 | 43.1102 | 0.74441 | 1.3146 | 0.38374
Dirty Non-Read | 10.6913 | 15.9344 | 2.3616 | 100 | 77.0494 | 37.131 | 37.5536 | 33.785 | 81.0226 | 28.5624 | 57.5397 | 20 | 19.6922 | 92.28 | 76.3483 | 46.8645 | 20.0064 | 7.1428 | 22.2222 | 65.2835 | 20.2532 | 19.6005 | 38.6285 | 3.303 | 1.8888
Clean Read | 11.9741 | 0.05832 | 25.634 | 0 | 3.8627 | 0.00292 | 1.7725 | 3.4931 | 0.0077 | 9.818 | 0 | 20 | 20.0531 | 1.817 | 0.64556 | 9.8173 | 0 | 64.2857 | 44.4444 | 0.06662 | 15.2833 | 24.2584 | 0.10808 | 2.1711 | 16.5115
Clean Non-Read | 74.2309 | 29.7998 | 62.1544 | 0 | 17.667 | 62.7926 | 60.0359 | 31.8311 | 18.9696 | 61.2617 | 40.4762 | 20 | 49.9975 | 3.2153 | 18.8407 | 43.0147 | 79.9936 | 28.5714 | 16.6667 | 34.6498 | 49.3988 | 13.0308 | 60.519 | 93.2114 | 81.2159
On average 37.4% blocks are dirty non-read and
42% blocks are clean non-read

## Slide 37: Single Core Performance
5% speedup over the whole SPECCPU2006 benchmarks
Chart: Speedup vs. Baseline LRU
| DIP | RRIP | SUP+ | RRP | RWP
 | 1.034 | 1.035 | 1.039 | 1.058 | 1.051
2.6KB
48.4KB
+2.3%
+1.6%
-0.7%

## Slide 38
Chart: Speedup vs. Baseline LRU
| 400.perlbench | 429.mcf | 434.zeusmp | 435.gromacs | 437.leslie3d | 450.soplex | 471.omnetpp | 481.wrf | 482.sphinx3 | 483.xalancbmk | GmeanMem | GmeanSPEC
DIP | 1 | 1.06 | 1 | 1 | 1 | 1.03 | 1 | 1.06 | 1.33 | 1.68 | 1.099 | 1.034
RRIP | 1.0403 | 1.06 | 1.0162 | 1.0113 | 0.95 | 1.0209 | 0.9848 | 1.0891 | 1.3521 | 1.68 | 1.102 | 1.035
SUP+ | 1.1148 | 1.0281 | 1.0348 | 1.0056 | 1.0131 | 1.0581 | 0.95 | 1.0494 | 1.542 | 1.6861 | 1.126 | 1.039
RRP | 1.1509 | 1.2493 | 1.0284 | 1.0086 | 1.0532 | 1.068 | 0.96366 | 1.1618 | 1.5078 | 1.7868 | 1.176 | 1.058
RWP | 1.1579 | 1.1399 | 1.0235 | 1.0182 | 1.0021 | 1.0205 | 0.97603 | 1.0736 | 1.4113 | 1.88 | 1.1461 | 1.051
Speedup
On average 14.6% speedup over baseline
5% speedup over the whole SPECCPU2006 benchmarks

## Slide 39: Writeback Traffic to Memory
Chart: Writeback Traffic Normalized to LRU
| 400.perlbench | 429.mcf | 434.zeusmp | 435.gromacs | 437.leslie3d | 450.soplex | 471.omnetpp | 481.wrf | 482.sphinx3 | 483.xalancbmk | GmeanMem | GmeanAll
RRP | 0.40724 | 0.97626 | 0.99374 | 1.0331 | 0.99454 | 0.87051 | 1.0148 | 0.86173 | 0.15386 | 0.84027 | 0.72469 | 0.91532
RWP | 1.3 | 0.99706 | 0.95561 | 1.1274 | 1.0242 | 1.2413 | 0.98323 | 0.99677 | 1.2487 | 1.3 | 1.1362 | 1.1755
Increases traffic by 17%
over the whole SPECCPU2006 benchmarks

## Slide 40: 4-Core Performance
Chart: Workloads
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0
RRP | 0.99553 | 1.0045 | 1.0121 | 1.0194 | 1.0224 | 1.0256 | 1.0263 | 1.0331 | 1.0372 | 1.0374 | 1.0401 | 1.0586 | 1.0604 | 1.0629 | 1.0717 | 1.0724 | 1.0828 | 1.0868 | 1.1009 | 1.1034 | 1.1091 | 1.1101 | 1.1101 | 1.1107 | 1.1217 | 1.1262 | 1.1277 | 1.1349 | 1.1357 | 1.1388 | 1.1529 | 1.155 | 1.1721 | 1.3607
RWP | 1.0969 | 1.0129 | 1.1034 | 1.0412 | 1.0374 | 1.0226 | 1.0135 | 1.0091 | 1.0195 | 1.0375 | 1.066 | 1.0022 | 1.0228 | 1.0081 | 1.0184 | 1.041 | 1.0183 | 1.0564 | 1.055 | 1.0234 | 1.0351 | 1.0791 | 1.1029 | 1.0337 | 1.1039 | 1.0319 | 1.022 | 1.037 | 1.0739 | 1.0775 | 1.0974 | 1.0976 | 1.235 | 1.2286

## Slide 41: Change of IPC with Static Partitioning
Chart: Xalancbmk
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
IPC | 0.839 | 0.776 | 0.7168 | 0.6667 | 0.6125 | 0.567 | 0.5366 | 0.5155 | 0.5005 | 0.4911 | 0.4865 | 0.4849 | 0.4846 | 0.4846 | 0.4846 | 0.4846 | 0.4846
Chart: Soplex
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
IPC | 0.5946 | 0.6085 | 0.6252 | 0.647 | 0.6691 | 0.6871 | 0.7005 | 0.7102 | 0.7162 | 0.72 | 0.7217 | 0.7228 | 0.7239 | 0.7242 | 0.7199 | 0.7031 | 0.6597