## Slide 1
Fast and Energy-Efficient In-DRAM
Bulk Data Copy and Initialization
RowClone
Vivek Seshadri, Yoongu Kim, Chris Fallin, Donghyuk Lee, Rachata Ausavarungnirun, Gennady Pekhimenko, Yixin Luo, Onur Mutlu, Phillip B. Gibbons*, Michael A. Kozuch*, Todd C. Mowry
Carnegie Mellon University *Intel Pittsburgh
Chart: Compared to Baseline
| bootup | compile | forkbench | mcached | mysql | shell
IPC Improvement | 0.15 | 0.09 | 0.43 | 0.04 | 0.04 | 0.4
Memory Energy Reduction | 0.4 | 0.32 | 0.6 | 0.15 | 0.17 | 0.67
Single Core Results
Memory Bandwidth Bottleneck
Bulk Copy and Initialization
Memory
Channel
Core
Core
MC
Limited Bandwidth
High Energy
abcdexyzjk
abcdexyzjk
aaaaaaaaaa
a
› Triggered frequently by many applications
› Consume high latency, bandwidth, and energy
› Do not require any computation
DRAM Chip Organization and Operation
Memory Channel
Chip I/O
Bank
Bank I/O
Subarray
Row Buffer
Row of DRAM cells (8Kb)
Even a single cell (orange) access transfers an entire row of data from the cells to the row buffer.
RowClone – Fast Parallel Mode (FPM)
0
Activate when
precharged
Activate when
activated
2-step row-to-row copy
r
c
r
o
w
s
s
t
o
w
d
r
Row Buffer
1
2
+ 11.6X latency reduction, 74.4X energy reduction
– src and dst in same subarray, only full row copy
Pipelined Serial Mode (PSM)
Chip I/O
src
dst
› Bank-to-bank cacheline copy
› Overlap read/write using shared bus
› 1.9X latency, 3.2X energy reduction
System Design
Forking
000000000000
Page zero
Checkpoint
VM Cloning
› ISA: memcpy and meminit
› µArch: manage coherence
› OS: smart page mapping
Primitives and Applications Accelerated by RowClone
Copy-on-Write
Bulk Zeroing
Chart: Compared to Baseline
| 2-Core | 4-Core | 8-Core
System Performance | 0.15 | 0.2 | 0.27
Memory Energy Efficiency | 0.19 | 0.17 | 0.17
Multi-Core Results
Copy/Zero Intensive Apps
Chart: Fraction of Memory Traffic
| bootup | compile | forkbench | mcached | mysql | shell
Read | 0.27394 | 0.34894 | 0.054305 | 0.45435 | 0.43893 | 0.099545
Write | 0.27185 | 0.33217 | 0.32279 | 0.45421 | 0.43769 | 0.089756
Copy | 0.21551 | 0 | 0.61578 | 0 | 0 | 0.42016
Zero | 0.23871 | 0.31889 | 0.007122 | 0.091442 | 0.12338 | 0.39054
Copy/Zero intensive applications run alongside memory intensive applications from SPEC CPU 2006
½
0
1
0
1
0
1
Overall DRAM area cost = 0.01%
Our Approach: Perform them in DRAM