## Slide 1: TRRespass: Exploiting the Many Sides of Target Row Refresh
Pietro Frigo1 Emanuele Vannacci1 Hasan Hassan2 Victor Van der Veen3 Onur Mutlu2 Herbert Bos1 Cristiano Giuffrida1 Kaveh Razavi1
1Vrije Universiteit Amsterdam 2ETH Zürich 3Qualcomm Technologies Inc.

## Slide 2: Teaser
Memory vendors advertise RowHammer-free devices
What is Target Row Refresh (TRR)? Not a single mitigation!
Reverse-engineering of in-DRAM mitigations
  The Many-sided RowHammer
  Hammering up to 20 aggressor rows
3 major vendors all vulnerable: Samsung, Micron, SK Hynix
  Currently representing over 95% of the DRAM market

## Slide 3: Memory request flow
CPU
Memory Controller
DRAM commands
DIMMs
DRAM

## Slide 4: DRAM Refresh
DRAM is dynamic because data must be refresh periodically
  Retention time (i.e., 64ms)
The MC issues a REFRESH command every 7.8µs
  Only a small portion of memory is refreshed with a command
  8192 refreshes within a 64ms interval

## Slide 5: Memory array
1
1
1
1
1
1
1
1
0
1
0
Row buffer
1
0
1
1
0
Row 1
Row 2
Row 3
Row 0

## Slide 6: Read operation: Row 1
ACTIVATE Row 1
1
1
1
1
1
1
1
1
0
1
0
1
-
-
-
-
Row 1
Row 2
Row 3
Row 0
0
1
1
0

## Slide 7: Read operation: Row 3
PRECHARGE Row 1
1
1
1
1
1
1
1
1
0
1
0
1
0
1
1
0
Row 1
Row 2
Row 3
Row 0
-
-
-
-

## Slide 8: Read operation: Row 3
ACTIVATE Row 3
1
1
1
1
1
1
1
1
-
-
-
-
0
1
1
0
Row 1
Row 2
Row 3
Row 0
0
1
0
1

## Slide 9: RowHammer
Bit flip!
1
1
1
1
1
0
1
1
0
1
0
1
0
1
1
0
Row 1
Row 2
Row 3
Row 0
-
-
-
-

## Slide 10: Double-sided RowHammer
Bit flip!
1
1
1
1
1
0
1
1
0
1
0
1
0
1
1
0
Row 1
Row 2
Row 3
Row 0
-
-
-
-
Aggressor row
1
1
1
1
Aggressor row
Victim row

## Slide 11: Hardware mitigations
Error-correcting code (ECC) [1]
Refreshing a row restores the cells electric charge: it prevents flips.
Double refresh
Target Row Refresh (TRR)
[1] L. Cojocaret al., “Exploiting Correcting Codes: On the Effectiveness of ECC Memory Against Rowhammer Attacks,” in S&P, 2019.

## Slide 12: Target Row Refresh
TRR-like mitigations track rows activations and refresh victim rows
  Many possible implementations in practice
  Security through obscurity
Pseudo TRR (pTRR)
  Memory controller implementation
In-DRAM TRR
  Embedded in the DRAM circuitry

## Slide 13: Timeline
'12
'14
'15
'13
'16
'18
'17
'19
pTRR DDR3
Intel reports pTRR on DDR3 server systems
pTRR DDR4
First DDR4 generation is pTRR protected
In-DRAM TRR
Earliest manufacturing date of RH-free DRAM modules
Last generation DIMMs we focus on

## Slide 14: Goals
Reverse engineer TRR to demystify in-DRAM mitigations
Memory device assessment
  A Novel hammering pattern: The Many-sided RowHammer
  Hammering up to 20 aggressor rows allows to bypass TRR
Automatically test memory devices: TRRespass
  Automate hammering patterns generation

## Slide 15: Challenges
Analysis from the CPU side not possible
  No timing side-channels
FPGA-based memory controller [1,2]
[1] H. Hassan et al., “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” in HPCA, 2017
[2] SAFARI Research Group, “SoftMC — GitHub Repository,” https:// github.com/CMU-SAFARI/SoftMC.

## Slide 16: Building blocks
Abstractions:
Sampler
  Track aggressor rows activations
  Keep a set of rows
Inhibitor
  Prevent bit flips
  Refresh victims

## Slide 17: Case study: Vendor C
How big is the sampler?
Pick N aggressor rows
Perform a series of hammers (activations of aggressors)
  8K activations
After each series of hammers, issue R refreshes
10 Rounds
Activations
Refreshes
Activations
Refreshes
Round

## Slide 18: Case study: Vendor C

## Slide 19: Case study: Vendor C

## Slide 20: Case study: Vendor C

## Slide 21: Case study: Observations
The TRR mitigation acts on every refresh command

## Slide 22: Case study: Vendor C

## Slide 23: Case study: Vendor C

## Slide 24: Case study: Observations
The TRR mitigation acts on every refresh command
The mitigation can sample more than one aggressor per refresh interval
The mitigation can refresh only a single victim within a refresh operation

## Slide 25: Case study: Vendor C

## Slide 26: Case study: Vendor C

## Slide 27: Case study: Observations
The TRR mitigation acts on every refresh command
The mitigation can sample more than one aggressor per refresh interval
The mitigation can refresh only a single victim within a refresh operation
Sweeping the number of refresh operations and aggressor rows while hammering reveals the sampler size

## Slide 28: Case study: Vendor C
with tREFi == 7.8μs
Notes: Discuss the sampler address dependency here, explaining that we've made further studies on other DIMMs, and we have additional observations.
Maybe add a slide after this one to summarize the key observations.

## Slide 29: Case study: Observations
The TRR mitigation acts on every refresh command
The mitigation can sample more than one aggressor per refresh interval
The mitigation can refresh only a single victim within a refresh operation
Sweeping the number of refresh operations and aggressor rows while hammering reveals the sampler size
The sampling mechanism is affected by the addresses of aggressor rows

## Slide 30: TRRespass: The RowFuzzer
Black-box fuzzing for RowHammer
  Ignore the MC optimizations
  Scalable approach for testing
The sampler can track a limited number of aggressor rows
  # Aggressors
The sampler design may be row address dependent
  Aggressor Location

## Slide 31: TRRespass: Results
42 DIMMS from 3 of the major vendors: Samsung, Micron, SK Hynix
  95% of the market
Testing 256MB of contiguous memory against the best pattern
13 DIMMs with bit flips
  Multiple effective patterns for each of them
Bit flips with double refresh
Fuzzing is effective.
  How to Improve? Parameter selection.

## Slide 32: Exploitation
Memory templating
  Find the right hammering pattern
  Locations of aggressors not always fundamental
Bit flips are repeatable
  Spurious flips
We demonstrate the feasibility of 3 example attacks:
  Privilege escalation [1]
  Access to co-hosted VM via RSA key corruption [2]
  Sudo exploit: opcode flipping [3]
[1] M. Seaborn and T. Dullien, “Exploiting the DRAM Rowhammer Bug to Gain Kernel Privileges,” in Black Hat USA, 2015
[2] K. Razavi et al., “Flip Feng Shui: Hammering a Needle in the Software Stack,” in USENIX Sec., 2016
[3] D. Gruss et al., “Another Flip in the Wall of Rowhammer Defenses,” in S&P, 2018.

## Slide 33: Conclusion
Bit flips with more than 20 aggressor rows!
  DDR4 devices are much more vulnerable than DDR3
  Bit flips with less than 50K activations
Fuzzing can help in memory testing
  Reverse engineering to find meaningful parameters
RowHammer is still a serious problem
No prompt mitigations available

## Slide 34
Questions!