## Slide 1: Simultaneous Multi-Layer Access Improving 3D-Stacked Memory Bandwidth at Low Cost
Donghyuk Lee, Saugata Ghose, Gennady Pekhimenko, Samira Khan, Onur Mutlu
Carnegie Mellon University
HiPEAC 2016

## Slide 2
cell array
peripheral logic
DRAM layer
DRAM layer
DRAM layer
DRAM layer
Executive Summary
In 3D-stacked DRAM, we want to leverage high bandwidth
  TSVs provide a huge opportunity
  In-DRAM bandwidth does not match
Problem: Global structures in layer very expensive – can’t replicate
Our Solution: Simultaneous Multi- Layer Access (SMLA)
  Use multiple layers at once to overcome bottleneck
  Requires smart multiplexing
  Two alternatives:
Evaluation vs. Wide I/O (16 core): 55% speedup, 18% DRAM energy reduction, negligible area overhead
Through-silicon vias
(TSVs)
Dedicated-IO,
Cascaded-IO
Notes: TSVs are not the problem
Global structures inside DRAM layer are actually expensive – can’t replicate

## Slide 3
Outline
2. Cascaded-IO
Performance Evaluation
Limited Bandwidth in 3D DRAM
Simultaneous Multi-Layer Access
1. Dedicated-IO
Limited Bandwidth in 3D DRAM

## Slide 4
Connecting Layers in 3D-Stacked DRAM
cell array
peripheral logic
DRAM layer
μ-bump
through-silicon vias (TSVs)
3D-stacked DRAM: 512 – 4K TSVs
Traditional 2D DRAM: 64-bit bus
8x – 64x increase – Can we exploit this?
Notes: Huge potential for BW increase

## Slide 5
accessed layer
If TSVs provide 16x bus width vs. 2D, do we get 16x bandwidth from the DRAM?
How Much Can Bandwidth Increase?
Can each layer deliver 16x the data?
cell array
peripheral logic

## Slide 6
peripheral
logic
bank
bank
sense amp.
sense amp.
Global sense amplifiers
Global bitlines
Data path
TSVs  X16
 X16?
 X16?
 X16?
How Much Can Bandwidth Increase?
cell
array
Global sense amplifiers and global bitlines are costly
 Cannot provide 16x in-DRAM BW  Bottleneck
Notes: Very large
Ex.: GSA more than 100x size of DRAM cell

## Slide 7
Our Goal
Design a new 3D-stacked DRAM that supplies high DRAM bandwidth at low cost
Problem
Limited in-DRAM bandwidth, leading to high costs for high-bandwidth 3D-stacked DRAM
Our Approach
Simultaneous Multi-Layer Access (SMLA)

## Slide 8
Outline
2. Cascaded-IO
Performance Evaluation
Limited Bandwidth in 3D DRAM
Simultaneous Multi-Layer Access
1. Dedicated-IO
Limited Bandwidth in 3D DRAM
Simultaneous Multi-Layer Access

## Slide 9
CHALLENGE: How to avoid TSV channel conflicts?
CHALLENGE: How to avoid TSV channel conflicts?
 Space Multiplexing & Time Multiplexing
Exploit in-DRAM bandwidth across idle layers by accessing multiple layers simultaneously
Simultaneous Multi-Layer Access
accessed layer
idle
idle
idle

## Slide 10
Outline
2. Cascaded-IO
Performance Evaluation
Limited Bandwidth in 3D DRAM
Simultaneous Multi-Layer Access
1. Dedicated-IO
Simultaneous Multi-Layer Access
1. Dedicated-IO

## Slide 11
Dedicated-IO: Space Multiplexing
Dedicate a subset of TSVs for each layer 
Transfer each layer’s data with narrower & faster IO
4X bandwidth
4X IO frequency
use 1/4 TSVs per layer

## Slide 12
Dedicated-IO: Two Problems
1. Differences in layers  Fabrication difficulties
Use 1/4 TSVs with 4X IO freq.
2. Weaker power network at upper layers
Power delivery
Notes: No changes in TSV design

## Slide 13
2. Cascaded-IO
1. Dedicated-IO
Outline
2. Cascaded-IO
Performance Evaluation
Limited Bandwidth in 3D DRAM
Simultaneous Multi-Layer Access
1. Dedicated-IO

## Slide 14
Cascaded-IO: Time Multiplexing
Layer 3
Layer 2
Layer 1
Layer 0
Segment TSVs to move data through
3D stack one layer at a time at 4F frequency
B bytes
B bytes
B bytes
B bytes

## Slide 15
Cascaded-IO: Time Multiplexing
Layer 3
Layer 2
Layer 1
Layer 0
B bytes
B bytes
B bytes
B bytes
Different throughput requirements for each layer
 Reduce IO frequency in upper layers
B
B
B
B
Throughput
2B
2B
2B
3B
3B
4B
IO Freq.
F
2F
3F
4F
Energy: 14% ↓

## Slide 16
Cascaded-IO Data Multiplexer
data
clock
latch
mux
ctrl.
counter
en.
Cascaded-IO Clock Propagator
cell array &
peripheral logic

## Slide 17
Outline
2. Cascaded-IO
Performance Evaluation
Limited Bandwidth in 3D DRAM
Simultaneous Multi-Layer Access
1. Dedicated-IO
2. Cascaded-IO
Performance Evaluation

## Slide 18
CPU: 4-16 cores
  Simulator: Instruction-trace-based x86 simulator
  3-wide issue, 512kB cache slice per core
Memory: 4 DRAM layers
  Simulator: Ramulator [Kim+ CAL 2015] https://github.com/CMU-SAFARI/ramulator
  64-entry read/write queue, FR-FCFS scheduler
  Energy Model: built from other high-frequency DRAMs
  Baseline: Wide I/O 3D-stacked DRAM, 200 MHz
Workloads
  16 multiprogrammed workloads for each core count
  Randomly selected from TPC, STREAM, SPEC CPU2000
Evaluation Methodology

## Slide 19
SMLA Improves Performance
Chart: 
| 4-core | 8-core | 16-core
Dedicated-IO (4X) | 14.35 | 28.28 | 50.43
Cascaded-IO (4X) | 18.16 | 32.91 | 55.75
Performance Improvement (%)
over Wide I/O 3D-stacked DRAM
55%
Notes: When bandwidth is low,
Dedicated-IO: all requests take longest time
Cascaded-IO: avg. save 2ns, range from 1-4

## Slide 20
SMLA Reduces Memory Energy
Chart: 
| 4-core | 8-core | 16-core
Dedicated-IO (4X) | 1.1 | 8.14 | 15.83
Cascaded-IO (4X) | 1.89 | 9.44 | 17.87
Memory Energy Reduction (%)
over Wide I/O 3D-stacked DRAM
18%

## Slide 21
Summary of Results
Significant performance improvement and DRAM energy reduction
Area overhead: ~3k transistors for 4-layer chip w/ 70mm2 layers (1024 TSVs)
Other Results & Analyses in the Paper
  Single-core results
  Standby power analysis
    Upper layers of Cascaded-IO use less power
  Thermal study
    SMLA stays within DRAM operating range
  Rank organization analysis
  Scalability analysis for more DRAM layers

## Slide 22
Conclusion
Through-silicon vias (TSVs) offer high bandwidth in 3D-stacked DRAM
Problem
  In-DRAM bandwidth limits available IO bandwidth in 3D-stacked DRAM
Our Solution: Simultaneous Multi-Layer Access (SMLA)
  Exploit in-DRAM bandwidth available in other layers by accessing multiple layers simultaneously
  Dedicated-IO
    Divide TSVs across layers, clock TSVs at higher frequency
  Cascaded-IO
    Pipelined data transfer through layers
    Reduce upper layer frequency for lower energy
Evaluation
  Significant performance improvement with lower DRAM energy consumption (55%/18% for 16-core) at negligible DRAM area cost

## Slide 23
Donghyuk Lee, Saugata Ghose, Gennady Pekhimenko, Samira Khan, Onur Mutlu
Carnegie Mellon University
HiPEAC 2016
We will release the SMLA source code by February.
Simultaneous Multi-Layer Access Improving 3D-Stacked Memory Bandwidth at Low Cost

## Slide 24
SMLA vs. HBM
HBM (High-Bandwidth Memory)
  Used in GPUs today
  Much wider bus than other 3D-stacked DRAMs (4096 TSVs vs. 1024 for Wide I/O)
  Double the global bitline count of Wide I/O
  Simultaneously access two bank groups: double the global sense amplifiers
HBM adds more bandwidth by scaling up resources (i.e., at higher cost)
  Each layer now gets two dedicated 128-bit channels
  Similar to Dedicated-IO, but more TSVs/global bitlines instead of faster TSVs
SMLA delivers higher bandwidth than HBM w/o extra bitlines/TSVs (at lower cost)
  Dedicated-IO: performance, energy efficiency similar to HBM; cost is lower
  Cascaded-IO: higher performance, energy efficiency; lower cost than HBM
Notes: Bank groups similar to LPDDR3, DDR4
Bank group approach orthogonal to SMLA

## Slide 25
Scaling SMLA to Eight Layers
Dedicated-IO
  Double the TSVs
    Same # of TSVs per layer
    2x total DRAM bandwidth of 4-layer SMLA
  Pairs of layers share a single set of TSVs
    Creates a layer group
    Same total DRAM bandwidth as 4-layer SMLA
Cascaded-IO
  Double the TSVs – 2 groups, 4 layers each
  Two groups, but sharing the TSVs
    Groups necessary to stay within burst length, limit multi-layer traversal time
    Same total DRAM bandwidth as 4-layer SMLA

## Slide 26
cell array
periphery
Conventional DRAM
data bus
IO Bandwidth = Bus Width X Wire Data Rate
Limited package pins
clock frequency
bank
peripheral logic
bank
bank

## Slide 27
Cascaded-IO Operation
data
clock
latch
ctrl.
data
clock
latch
cell array &
peripheral logic
cell array &
peripheral logic
mux
ctrl.
mux
counter
en.
counter
en.
2F
F
data
data
2B
B

## Slide 28
Estimated Energy Consumption
Chart: 
| 1066 | 1333 | 1600 | 1866
IDD1 (Active: Activation/Read/Precharge) | 50 | 54 | 56 | 58
IDD2P (Precharge Power-Down) | 12 | 12 | 12 | 12
IDD3P (Active Power-Down) | 22 | 22 | 22 | 22
IDD2N (Precharge Standby) | 29 | 32 | 34 | 36
IDD3N (Active Standby) | 31 | 33 | 35 | 37
1066
1333
1600
1866
Data Channel Frequency (MHz)
Current (mA)
Standby currents are proportional to data channel frequency  Cascaded-IO reduces standby current

## Slide 29
Standby Power Consumption
Chart: 
| layer 0 | layer 1 | layer 2 | layer 3 | mean | layer 0 | layer 1 | layer 2 | layer 3 | mean | layer 0 | layer 1 | layer 2 | layer 3 | mean | layer 0 | layer 1 | layer 2 | layer 3 | mean | 3D-Stakced (400) | 3D-Stacked (1600) | Dedicated-IO (1600) | Cascaded-IO (1600)
Standby | 6.945 | 6.945 | 6.945 | 6.945 | 6.945 | 10.42 | 10.42 | 10.42 | 10.42 | 10.42 | 10.42 | 10.42 | 10.42 | 10.42 | 10.42 | 10.42 | 10.42 | 8.105 | 6.945 | 8.9725
Standby Current (mA)
Cascaded-IO provides standby power reduction due to reduced upper layer frequency
14%
Wide I/O
Wide I/O
Notes: In logical, system consists of processor, main memory and IO devices.
Processor accesses main memory for get data for executing instruction, referred to as CPU access, and
IO devices accesses main memory to provide its data to main memory.
Therefore, the main memory connects processor and IO devices as an intermediary layer.
TO FIX: typo on 400

## Slide 30
Thermal Analysis
Temperature (°C)
Chart: 
| layer 0 | layer 1 | layer 2 | layer 3 | layer 0 | layer 1 | layer 2 | layer 3 | layer 0 | layer 1 | layer 2 | layer 3 | layer 0 | layer 1 | layer 2 | layer 3 | 3D-Stacked (200MHz) | 3D-Stacked (1600MHz) | Dedicated-IO (1600MHz) | Cascaded-IO (1600MHz)
Temperature | 47.19 | 47.2 | 47.17 | 47.15 | 60.24 | 60.19 | 60.09 | 59.94 | 65.56 | 65.47 | 65.3 | 65.07 | 59.49 | 59.45 | 59.37 | 59.26
Cascaded-IO reduces operating temperature due to reduced upper layer frequency
Wide I/O
Wide I/O
Notes: In logical, system consists of processor, main memory and IO devices.
Processor accesses main memory for get data for executing instruction, referred to as CPU access, and
IO devices accesses main memory to provide its data to main memory.
Therefore, the main memory connects processor and IO devices as an intermediary layer.