## Slide 1: Solar-DRAM: Reducing DRAM Access Latency by Exploiting the Variation in Local Bitlines
Jeremie S. Kim Minesh Patel
Hasan Hassan Onur Mutlu
Notes: Hi, my name is Jeremie Kim and I will be presenting Solar-DRAM, a mechanism for reducing DRAM access latency by exploiting the variation in local bitlines. [CLICK]

## Slide 2
  Motivation: DRAM latency is a major performance bottleneck
  Problem: Many important workloads exhibit bank conflicts in DRAM, which result in even longer latencies
  Goal:
  Rigorously characterize access latency on LPDDR4 DRAM
  Exploit findings to robustly reduce DRAM access latency
  Solar-DRAM:
  Categorizes local bitlines as “weak (slow)” or “strong (fast)”
  Robustly reduces DRAM access latency for reads and writes to data contained in “strong” local bitlines.
Evaluation:
Experimentally characterize 282 real LPDDR4 DRAM chips
In simulation, Solar-DRAM provides 10.87% system performance improvement over LPDDR4 DRAM
Executive Summary
Notes: To begin, I will give a brief overview. [CLICK] DRAM latency is a major performance bottleneck in modern computer systems. [CLICK] The problem is that many important workloads exhibit many bank conflicts in DRAM which result in even longer latencies [CLICK] The goal is to [CLICK] first, rigorously characterize access latency on state-of-the-art LPDDR4 DRAM and [CLICK] second, exploit our findings to robustly reduce DRAM access latency. From our findings, we propose [CLICK] Solar-DRAM, a mechanism that [CLICK] identifies local bitlines as weak or strong and [CLICK] robustly reduces DRAM access latency for reads and writes depending on whether it is to data contained in strong local bitlines. In order to [CLICK] evaluate Solar-DRAM, we [CLICK] experimentally characterize 282 real LPDDR4 DRAM modules, and [CLICK] show in simulation that Solar-DRAM provides 10.87% system performance improvement over LPDDR4 DRAM [CLICK]

## Slide 3
Motivation and Goal
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Solar-DRAM
Evaluation
Conclusion
Solar-DRAM Outline
Notes: Here is the outline for the talk today [CLICK]

## Slide 4
Motivation and Goal
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Solar-DRAM
Evaluation
Conclusion
Solar-DRAM Outline
Notes: I’ll start off by discussing the motivation and goal [CLICK]

## Slide 5: Motivation and Goal
Many important workloads exhibit many bank conflicts
  Bank conflicts result in an additional delay of tRCD
  This negatively impacts overall system performance
A prior work (FLY-DRAM) finds weak (slow) cells and uses variable tRCD depending on cell strength, however
  They do not show the viability of static profile of cell strength
  They characterize an older generation (DDR3) of DRAM
Our goal is to
  Rigorously characterize state-of-the-art LPDDR4 DRAM
  Demonstrate viability of using static profile of cell strength
  Devise a mechanism to exploit more activation failure (tRCD) characteristics and further reduce DRAM latency
Notes: [CLICK] Many important workloads exhibit many bank conflicts. [CLICK] Bank conflicts result in an additional delay of tRCD, which is a timing parameter that must be obeyed for accesses to a closed DRAM row. [CLICK] This negatively impacts overall system performance.
[CLICK] A previously proposed mechanism called FLY-DRAM categorizes DRAM cells with regard to their strength in terms of how likely it is to fail when accessed with a tRCD below manufacturer-recommended values. Unfortunately, [CLICK] they do not show the viability of relying on a static profile of cell strength, such that a cell not contained in the profile will not fail and [CLICK] they characterize an older generation of DRAM.
[CLICK] Our goal is to [CLICK] rigorously characterize state-of-the-art LPDDR4 DRAM, [CLICK] demonstrate viability of using a static profile of cell strength, and [CLICK] devise a mechanism to exploit more activation failure characteristics and further reduce DRAM latency. [CLICK]

## Slide 6
Motivation and Goal
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Solar-DRAM
Evaluation
Conclusion
Solar-DRAM Outline
Notes: I will now give background on DRAM structure and operation [CLICK]

## Slide 7
DRAM Background
Each DRAM cell is made of 1 capacitor and 1 transistor
Wordline enables reading/writing data in the cell
Bitline moves data from cells to/from I/O circuitry
Notes: [CLICK] Each DRAM cell is comprised of 1 capacitor and 1 transistor. The capacitor stores data in the form of charge, and the access transistor gates movement of charge to and from the capacitor. [CLICK] The wordline enables the access transistor to allow reading and writing data in the cell. [CLICK] The bitline moves data to and from the DRAM cell and I/O circuitry, so it can be returned to the CPU. [CLICK]

## Slide 8
DRAM Bank
local
bitline
wordline
DRAM cell
DRAM row
A DRAM bank is organized hierarchically with subarrays
Columns of cells in subarrays share a local bitline
Rows of cells in a subarray share a wordline
DRAM Background
Notes: [CLICK] Each DRAM bank is organized hierarchically with subarrays. [CLICK] Each circle in the cartoon represents a single DRAM cell. [CLICK] columns of DRAM cells in a subarray are connected with a wire referred to as a local bitline. [CLICK] and rows of DRAM cells are connected with a wire referred to as a wordline, and [CLICK] a row of DRAM cells is called a DRAM row. [CLICK] at the peripherals of the core cell arrays are a local row decoder, which selects the row to read and write to, and a local row-buffer which amplifies the data that is stored in the cell to an I/O readable value. [CLICK] DRAM is comprised of many subarrays which are often composed of 512 to 1024 rows. [CLICK] Further peripherals exist containing the group of subarrays. The global row decoder selects the local row decoder that will drive the wordline, and the global row buffer buffers data, acting as a cache for DRAM accesses to the same row. [CLICK] We refer to the whole DRAM structure as a bank [CLICK]

## Slide 9
DRAM Operation
…
…
…
…
…
Local Row Buffer
Local Row Buffer
Cache line
READ
…
READ
READ
Row Decoder
Local Row Buffer
READ
READ
READ
ACT R0
RD
PRE R0
RD
RD
ACT R1
RD
RD
RD
Notes: Let’s take a look at how DRAM operates in the scope of a single subarray. [CLICK] Because memory controllers typically access DRAM at the granularity of a cache line, we combine consecutive, aligned DRAM cells as cache lines in our diagram. [CLICK] First, we activate the first row, which [CLICK] copies the entire rows' data into the row buffer. At this point, we can [CLICK] read our data at the granularity [CLICK] of cache lines within the [CLICK] activated or opened row. When we want to access data on another row, we must precharge [CLICK] the currently opened row, which prepares the row buffer for copying data from another row. We can now [CLICK] activate the second row, before reading data from it [CLICK][CLICK][CLICK]

## Slide 10
wordline
capacitor
access
transistor
bitline
Sense Amplifier
Vdd
0.5 Vdd
Bitline Voltage
Time
Ready to Access
Voltage Level
tRCD
Guardband
Process variation during manufacturing results in cells having unique behavior
Vmin
ACTIVATE
SA Enable
READ
Weak
(slow)
Strong
(fast)
Bitline Charge Sharing
DRAM Accesses and Failures
[Kim+ HPCA’18]
Notes: Now lets take a look at the timing parameters that must be obeyed to prevent failures. [CLICK] With this cartoon of a DRAM cell, we follow the voltage on the bitline. [CLICK][CLICK] The x-axis shows time and the y-axis shows the voltage on the bitline. [CLICK] Initially the bitline is kept at Vdd/2. [CLICK] When the wordline is driven high or activated, [CLICK] the capacitor begins to share charge with the bitline. The sense amplifier is then enabled and [CLICK] the voltage differential on the bitline is amplified to an I/O readable value. [CLICK] In order to ensure correctness of operation, the memory controller can only read data tRCD time after the activation. [CLICK] We could read this data earlier, when it reaches a readable voltage threshold (Vmin), [CLICK] but we want to make sure that there is enough guardband such that other cells that may be [CLICK] weaker due to process variation will not fail when accessed tRCD time after activation. [CLICK] We highlight and refer to varying degrees of strengths of cells in terms of how early they reach the readable voltage threshold.

## Slide 11
wordline
capacitor
access
transistor
bitline
SA
Vdd
0.5 Vdd
Bitline Voltage
Time
Ready to Access
Voltage Level
tRCD
Vmin
ACTIVATE
SA Enable
READ
Weaker cells have a higher probability to fail because they are slower
DRAM Accesses and Failures
Weak
(slow)
Strong
(fast)
[Kim+ HPCA’18]
Notes: If we are to read with a [CLICK] tRCD reduced below manufacturer-recommended values, we begin to induce failures in the weaker cell. Cells that are read when their bitline’s voltage is lower than Vmin, have a probability of failure. And this probability increases as you read further below the voltage threshold. We refer to these failures as activation failures. [CLICK]

## Slide 12
Recap of Goals
To identify the opportunity for reliably reducing tRCD, we want to:
  Rigorously characterize state-of-the-art LPDDR4 DRAM
  Demonstrate the viability of using static profile of cell strength
  Devise a mechanism to exploit more activation failure (tRCD) characteristics and further reduce DRAM latency
Notes: To reiterate our goals of reducing tRCD, we want to [CLICK] rigorously characterize state of the art LPDDR4 DRAM, [CLICK] demonstrate the viability of using a static profile of cell strength, and [CLICK] devise a mechanism to exploit more activation failure characteristics and further reduce DRAM latency.

## Slide 13
Motivation and Goal
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Solar-DRAM
Evaluation
Conclusion
Solar-DRAM Outline
Notes: I will now describe our methodology for experimentally testing our DRAM modules

## Slide 14
282 2y-nm LPDDR4 DRAM modules
  2GB device size
  From 3 major DRAM manufacturers
Thermally controlled testing chamber
  Ambient temperature range: {40°C – 55°C} ± 0.25°C
  DRAM temperature is held at 15°C above ambient
Precise control over DRAM commands and timing parameters
  Test reduced latency effects by reducing tRCD parameter
Ramulator DRAM Simulator [Kim+, CAL’15]
  Access latency characterization in real workloads
Experimental Methodology
Notes: The infrastructure we developed tested 282 state-of-the-art LPDDR4 DRAM chips.
Each device is [CLICK] 2 gigabytes in size, and we have chips from across [CLICK] three major DRAM vendors.
[CLICK] We test within a thermally controlled chamber with an [CLICK] ambient temperature range of 40 to 55 degrees C with a tolerance of 0.25 degrees. [CLICK] DRAM temperature is always held at 15 degrees C above ambient using a local heat source
[CLICK] We had precise control over DRAM commands and timing parameters
[CLICK] We experimentally characterized activation failures by reducing the tRCD timing parameter and accessing DRAM
[CLICK] Additionally, we used DRAM simulator Ramulator to study DRAM access patterns in real workloads.
[CLICK]

## Slide 15
Motivation and Goal
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Solar-DRAM
Evaluation
Conclusion
Solar-DRAM Outline
Notes: I will now present our key characterization results.

## Slide 16
Spatial distribution of activation failures
Spatial locality of activation failures
Distribution of cache accesses in real workloads
Short-term variation of activation failure probability
Effects of reduced tRCD on write operations
Characterization Results
Notes: I will present our results in the following order [CLICK] First, we’ll look at the spatial distribution of activation failures, [CLICK] next, we look at the spatial locality of activation failures for a single access, [CLICK] next we will look at the distribution of cache accesses in real workloads to study whether certain cache line offsets within a row are accessed immediately following an activation more frequently than others. This would indicate that some cache line offsets are affected by the tRCD timing parameter more than others. [CLICK] Next we look at whether the probability of activation failure changes over time. [CLICK] next, we look at the effects of reducing tRCD on write operations.

## Slide 17: Spatial Distribution of Failures
Activation failures are highly constrained
to local bitlines (i.e., subarrays)
1024
512
0
512
1024
DRAM Row (number)
Subarray Edge
DRAM Column (number)
How are activation failures spatially distributed in DRAM?
Notes: We first set out to answer [CLICK] How are activation failures spatially distributed in DRAM? We induce activation failures in many of our DRAM modules across all vendors and we find similar results. [CLICK] This plot is a representative bitmap of a 1024 by 1024 array of DRAM cells. We indicate DRAM cells that were seen to fail in black, and those that did not in white. We observe that failures are highly constrained to short columns of DRAM cells. Because modern DRAM uses subarrays containing between 512 and 1024 rows, we expect that [CLICK] the sudden change in columns with failures indicate subarray edges. [CLICK] we conclude that activation failures are highly constrained to local bitlines within subarrays. We refer to bitlines containing failures as weak bitlines [CLICK]

## Slide 18: Spatial Locality of Failures
Activation failures are constrained to the cache line
first accessed immediately following an activation
Where does a single access induce activation failures?
…
…
…
…
…
Local Row Buffer
Weak bitline
Local Row Buffer
Cache line
Row Decoder
READ
✘
✘
✘
✘
…
Notes: The next question, we want to answer is, [CLICK] where does a single access induce activation failures? To answer this question, we run the following test on [CLICK] many cache lines of DRAM with and without [CLICK] “weak bitlines”. We first [CLICK] activate [CLICK] the row containing the cache line, and then immediately read [CLICK] the data in the cache line. [CLICK] This results in failures. [CLICK] we observe that these failures only occur within the cache line that was accessed immediately following the activation, even if there were other weak bitlines in the row. [CLICK]

## Slide 19: Spatial Locality of Failures
Activation failures are constrained to the cache line
first accessed immediately following an activation
Where does a single access induce activation failures?
…
…
…
…
…
Local Row Buffer
Weak bitline
Local Row Buffer
Cache line
Row Decoder
READ
✘
✘
✘
✘
…
This shows that we can rely on a static profile of weak bitlines to determine whether an access will cause failures
We can profile regions of DRAM
at the granularity of cache lines within subarrays
(i.e., subarray column)
Notes: We conclude that we can identify regions of DRAM at the granularity of cache lines within subarrays as weak or strong. [CLICK]

## Slide 20: Distribution of Cache Accesses
Which cache line is most likely to be accessed first immediately following an activation?
…
…
…
…
…
Local Row Buffer
Cache line
Row Decoder
…
Cache line
offset 0
Cache line
offset 1
Cache line
offset 2
…
Notes: The next question we want to answer is [CLICK] ”Which cache line is most likely to be accessed first immediately following an activation?”. [CLICK] For our same subarray cartoon, we identify the granularity of weak regions in DRAM which [CLICK] span a cache line granularity within a subarray. [CLICK][CLICK][CLICK][CLICK] we refer to these as subarray columns.

## Slide 21: Distribution of Cache Accesses
In some applications, up to 22.2% of first accesses
to a newly-activated DRAM row
request cache line 0 in the row
Which cache line is most likely to be accessed first immediately following an activation?
Notes: Using various SPEC workloads mixes, we observe the probability that each cache line offset is accessed immediately following an activation. [CLICK] The x-axis shows the cache line offset accessed in a newly-activated DRAM row, and the y-axis shows the probability of each cache line offset being accessed. We note that a significant proportion of accesses immediately following activations go to the 0th cache line offset. [CLICK] In some applications, up to 22.2% of first accesses to a newly-activated DRAM row request cache line 0 in the row. [CLICK]

## Slide 22: Distribution of Cache Accesses
In some applications, up to 22.2% of first accesses
to a newly-activated DRAM row
request cache line 0 in the row
Which cache line is most likely to be accessed first immediately following an activation?
This shows that we can rely on a static profile of weak bitlines to determine whether an access will cause failures
tRCD generally affects cache line 0 in the row
more than other cache line offsets
Notes: This indicates that tRCD affects cache line 0 in the row more than any other cache line offset in the row. [CLICK]
####### Up to 6.54% with ONLY reducing tRCD of 0th cache line

## Slide 23
Short-term Variation
Does a bitline’s probability of failure (i.e., latency characteristics) change over time?
cells_in_SA_bitline: number of cells in a local bitline
num_iters: iterations we try to induce failures in each cell
num_iters_failedcelln: iterations celln fails in
We sample many times over a long period and plot how it varies across all samples
We sample Fprob many times over a long period and plot how Fprob varies across all samples
Notes: We next want to answer the question of [CLICK] whether the bitline’s probability of failure (or the latency characteristics) changes over time. We use [CLICK] failure probability or Fprob as a metric that we define to essentially quantify how weak or strong a subarray bitline is, as the proportion of times each cell in the bitline fails out of the total number of times every cell in the bitline is tested. [CLICK] cells_in_SA_bitline: is the number of cells in a local bitline. [CLICK] num_iters is the number of iterations we try to induce failures in each cell. [CLICK] and num_iters_failed indicates the number of iterations that cell_n fails in. A low Fprob indicates a strong bitline, and a high Fprob indicates a weak bitline. [CLICK] We sample Fprob many times over a long period and plot how Fprob varies across all samples. [CLICK]

## Slide 24
A weak bitline is likely to remain weak and
a strong bitline is likely to remain strong over time
Short-term Variation
Does a bitline’s probability of failure (i.e., latency characteristics) change over time?
Notes: [CLICK] For each bitline with an Fprob value at time 1 (on the x-axis), we plot the distribution of how Fprob is different at all other sample points. This distribution is plotted as a box-and-whiskers plot, where the box is plotted in blue and the whiskers are in orange. We note that the distributions tightly follow the x=y axis, which indicates that [CLICK] a weak bitline is likely to remain weak and a strong bitline is likely to remain strong over time. [CLICK]

## Slide 25
A weak bitline is likely to remain weak and
a strong bitline is likely to remain strong over time
Short-term Variation
Does a bitline’s probability of failure (i.e., latency characteristics) change over time?
This shows that we can rely on a static profile of weak bitlines to determine whether an access will cause failures
We can statically profile weak bitlines
and determine if an access in the future will cause failures
Notes: From this, we conclude that we can statically profile weak bitlines in DRAM once and use it to reliably determine whether an access will cause failures at any point in the future.

## Slide 26
We can reliably issue write operations
with significantly reduced tRCD (e.g., by 77%)
How are write operations affected by reduced tRCD?
Write Operations
…
…
…
…
…
Local Row Buffer
Weak bitline
Local Row Buffer
Cache line
Row Decoder
WRITE
…
✔
✔
✔
✔
Notes: The next question we want to answer is [CLICK] “How are write operations affected by a reduced tRCD?” To answer this question, we run the following test on [CLICK] many cache lines of DRAM with and without [CLICK] “weak bitlines”. We first [CLICK] activate [CLICK] the row containing the cache line, and then immediately write [CLICK][CLICK] to the cache line. We observe that the data is written correctly [CLICK] We experimentally find that we can reliably issue write operations with tRCD values reduced by up to 77% [CLICK]

## Slide 27
Motivation and Goal
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Solar-DRAM
Evaluation
Conclusion
Solar-DRAM Outline
Notes: Leveraging all of our findings from characterizing activation failures in real DRAM modules, we propose Solar-DRAM to reliably reduce activation latency. [CLICK]

## Slide 28: Solar-DRAM
Identifies subarray columns as “weak (slow)” or “strong (fast)” and accesses cache lines in strong subarray columns with reduced tRCD
Uses a static profile of weak subarray columns
  Obtained in a one-time profiling step
Three Components
  Variable-latency cache lines (VLC)
  Reordered subarray columns (RSC)
  Reduced latency for writes (RLW)
Notes: Solar-DRAM [CLICK] identifies subarray columns as weak or strong and accesses cache lines in strong subarray columns with reduced tRCD. [CLICK] Solar-DRAM uses a static profile of weak subarray columns, which can be [CLICK] obtained in a one-time profiling step as we showed in our characterization.
[CLICK] Solar-DRAM is comprised of three distinct components. [CLICK] Variable latency cache lines (VLC), [CLICK] Reordered subarray columns (RSC), and [CLICK] reduced latency for writes (RLW) [CLICK]

## Slide 29: Solar-DRAM
Identifies subarray columns as “weak (slow)” or “strong (fast)” and accesses cache lines in strong subarray columns with reduced tRCD
Uses a static profile of weak subarray columns
  Obtained in a one-time profiling step
Three Components
  Variable-latency cache lines (VLC)
  Reordered subarray columns (RSC)
  Reduced latency for writes (RLW)
Notes: I will now explain the three components starting with VLC. [CLICK]

## Slide 30: Solar-DRAM: VLC (I)
Row Decoder
Cache line
…
…
…
…
…
Identifies subarray columns comprised of strong bitlines
Access cache lines in strong subarray columns with a reduced tRCD
Local Row Buffer
Weak bitline
Strong bitline
Strong subarray
column
Notes: [CLICK] For each subarray, we identify local bitlines as [CLICK] weak or [CLICK] strong. VLC [CLICK] identifies cache lines fully comprised of strong bitlines and [CLICK] accesses such cache lines with a reduced tRCD.

## Slide 31: Solar-DRAM
Identifies subarray columns as “weak (slow)” or “strong (fast)” and accesses cache lines in strong subarray columns with reduced tRCD
Uses a static profile of weak subarray columns
  Obtained in a one-time profiling step
Three Components
  Variable-latency cache lines (VLC)
  Reordered subarray columns (RSC)
  Reduced latency for writes (RLW)
Notes: Now I will describe Reordered subarray columns or (RSC) [CLICK]

## Slide 32: Solar-DRAM: RSC (II)
Row Decoder
Cache line
…
…
…
…
…
Local Row Buffer
Cache line 0
Cache line 1
Cache line 0
Cache line 1
Remap cache lines across DRAM at the memory controller level so cache line 0 will likely map to a strong cache line
Strong subarray
column
Notes: [CLICK] From the same diagram, we see that [CLICK] Cache line 0 is weak, and Cache line 1 is strong. [CLICK] In order to capitalize on our knowledge that Cache line 0 is most often accessed immediately following an activation, RSC remaps cache lines across DRAM at the memory controller level so cache line 0 will likely map to a strong cache line such that it can be accessed with a reduced trcd. [CLICK]

## Slide 33: Solar-DRAM
Identifies subarray columns as “weak (slow)” or “strong (fast)” and accesses cache lines in strong subarray columns with reduced tRCD
Uses a static profile of weak subarray columns
  Obtained in a one-time profiling step
Three Components
  Variable-latency cache lines (VLC)
  Reordered subarray columns (RSC)
  Reduced latency for writes (RLW)
Notes: Now I will describe Reduced latency for writes (RLW) [CLICK]

## Slide 34: Solar-DRAM: RLW (III)
Strong subarray
column
Row Decoder
Cache line
Local Row Buffer
…
…
…
…
…
Write to all locations in DRAM with a significantly reduced tRCD (e.g., by 77%)
Cache lines do not fail with reduced tRCD
Notes: [CLICK] RLW essentially identifies all subarray columns as [CLICK] strong when writing to DRAM. In other words, [CLICK] cache lines do not fail when accessed with a tRCD reduced by up to 77%. [CLICK] RLW therefore writes to all locations in DRAM with a significantly reduced tRCD. [CLICK]

## Slide 35: Solar-DRAM: Putting it all Together
Each component increases the number of accesses that can be issued with a reduced tRCD
They combine to further increase the number of cases where tRCD can be reduced
Solar-DRAM utilizes each component (VLC, RSC, and RLW) in concert to reduce DRAM latency and significantly improve system performance
Notes: [CLICK] Each component increases the number of accesses that can be issued with a reduced tRCD. [CLICK] And they combine to further increase the number of cases where tRCD can be reduced. [CLICK] Solar-DRAM utilizes each of the components VLC, RSC, and RLW in concert to reduce average DRAM latency and significantly improve system performance.

## Slide 36
Motivation and Goal
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Solar-DRAM
Evaluation
Conclusion
Solar-DRAM Outline
Notes: I will now discuss our evaluation of Solar-DRAM [CLICK]

## Slide 37
Cycle-level simulator: Ramulator [Kim+, CAL’15] https://github.com/CMU-SAFARI/ramulator
4-core system with LPDDR4-3200 memory
Benchmarks: SPEC2006
  40 8-core workloads
Performance metric: Weighted Speedup (WS)
Evaluation Methodology
Notes: In order to evaluate Solar-DRAM and its three subcomponents, and compare it against the prior work FLY-DRAM, we simulate a 4-core system with LPDDR4 memory on Ramulator, a cycle-level simulator. We use 40 8-core workload mixes from SPEC2006 benchmark suite and compare the mechanisms with the weighted speedup performance metric. [CLICK]

## Slide 38
Evaluation: Homogeneous workloads
FLY-DRAM
4-core Homogeneous Workload Mixes
Weighted Speedup (%)
Notes: To show how each mechanism might perform on various DRAM modules with different numbers of weak subarray columns per bank, we sweep the number of weak subarray columns per bank on the x-axis and simulate each mechanism with 10 randomly chosen profiles per number of weak subarray columns, for each workload mix. In our conservative configuration, we have 1024 subarray columns per bank. Each of these speedups are aggregated into a box-and-whiskers plot. The y-axis shows the weighted speedup improvement as a percentage over LPDDR4 DRAM. We first study the performance benefit of FLY-DRAM. We note that because FLY-DRAM identifies weak regions of DRAM at the granularity of global bitlines across the full bank, FLY-DRAM’s performance benefits quickly diminish to 0 with a small number of weak subarray columns. [CLICK]

## Slide 39
Evaluation: Homogeneous workloads
FLY-DRAM
VLC
4-core Homogeneous Workload Mixes
Weighted Speedup (%)
4-core Homogeneous Workload Mixes
Notes: We next plot Variable latency cache lines or VLC. We note that with any number of weak subarray columns per bank, VLC alone outperforms FLY-DRAM, and continues to bring performance benefits with even 512 weak subarray columns per bank. [CLICK]

## Slide 40
Evaluation: Homogeneous workloads
FLY-DRAM
VLC
RSC
4-core Homogeneous Workload Mixes
Weighted Speedup (%)
Notes: We next show the performance benefit of Reordered subarray columns or RSC, and show that in many cases, the performance benefit increases over VLC. This is because RSC increases the proportion of accesses that use a reduced tRCD. [CLICK]

## Slide 41
Evaluation: Homogeneous workloads
FLY-DRAM
VLC
RSC
RLW
4-core Homogeneous Workload Mixes
Weighted Speedup (%)
Notes: We next plot the performance benefit of Reduced latency writes or RLW. We note that RLW performs the same regardless of the number of weak subarray columns per bank and so the distribution is the same regardless of the x-axis. We observe that RLW alone can bring up to 6.59% increase in weighted speedup over LPDDR4 DRAM. [CLICK]

## Slide 42
Evaluation: Homogeneous workloads
FLY-DRAM
VLC
RSC
RLW
Solar-DRAM
4-core Homogeneous Workload Mixes
Weighted Speedup (%)
Solar-DRAM reduces tRCD for more DRAM accesses
and provides 10.87% performance benefit
Notes: When we evaluate Solar-DRAM, the synergistic mechanism of VLC, RSC, and RLW, we observe a significant improvement in weighted speedup. At the ideal case, where there are no weak subarray columns in DRAM, Solar-DRAM provides up to 10.87% improvement in weighted speedup over LPDDR4. Even when half of the subarray columns are weak (shown when x equals 512), Solar-DRAM provides up to 8.8% performance benefit, where FLY-DRAM provides 0. From a characterization of real LPDDR4 DRAM modules, we find that we should expect 2.8% of subarray columns to be weak on average. In our configuration, [CLICK] this falls between having 16 and 64 weak subarray columns per bank. At this point, FLY-DRAM’s performance benefit diminishes to 0, but Solar-DRAM maintains high benefits showing that Solar-DRAM can bring performance improvement to a larger number of DRAM modules that may have a high number of weak subarray columns. [CLICK] Solar DRAM reduces tRCD for more DRAM accesses than FLY-DRAM and provides up to 10.87% performance benefit across many DRAM modules. [CLICK]
2.8% average number of weak subarray bitlines per bank

## Slide 43
A detailed analysis on:
  Devices of the three major DRAM manufacturers
  Data Pattern Dependence of activation failures
    Random data pattern finds the highest coverage of weak bitlines
  Temperature effects on activation failure probability
    Fprob generally increases with higher temperatures
  Evaluation with Heterogeneous workloads
    Solar-DRAM provides 8.79% performance benefit
Further discussion on:
  Implementation details
  Finding a comprehensive profile of weak subarray columns
Other Results in the Paper

## Slide 44
Motivation and Goal
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Solar-DRAM
Evaluation
Conclusion
Solar-DRAM Outline
Notes: To Conclude [CLICK]

## Slide 45
  Motivation: DRAM latency is a major performance bottleneck
  Problem: Many important workloads exhibit bank conflicts in DRAM, which result in even longer latencies
  Goal:
  Rigorously characterize access latency on LPDDR4 DRAM
  Exploit findings to robustly reduce DRAM access latency
  Solar-DRAM:
  Categorizes local bitlines as “weak (slow)” or “strong (fast)”
  Robustly reduces DRAM access latency for reads and writes to data contained in “strong” local bitlines.
Evaluation:
Experimentally characterize 282 real LPDDR4 DRAM chips
In simulation, Solar-DRAM provides 10.87% system performance improvement over LPDDR4 DRAM
Executive Summary
Notes: [CLICK] DRAM latency is a major performance bottleneck in modern computer systems. [CLICK] The problem is that many important workloads exhibit many bank conflicts which result in even longer latencies. [CLICK] The goal is to [CLICK] first, rigorously characterize access latency on state-of-the-art LPDDR4 DRAM and [CLICK] second, exploit our findings to robustly reduce DRAM access latency. From our findings, we propose [CLICK] Solar-DRAM, a mechanism that [CLICK] identifies local bitlines as weak or strong and robustly reduces DRAM access latency for reads and writes depending on whether it is to data contained in strong local bitlines. In order to [CLICK] evaluate Solar-DRAM, we [CLICK] experimentally characterize 282 real LPDDR4 DRAM modules, and [CLICK] show in simulation that Solar-DRAM provides 10.87% system performance improvement over LPDDR4 DRAM [CLICK]

## Slide 46: Solar-DRAM: Reducing DRAM Access Latency by Exploiting the Variation in Local Bitlines
Jeremie S. Kim Minesh Patel
Hasan Hassan Onur Mutlu

## Slide 47
4-core Heterogeneous Workload Mixes
Weighted Speedup (%)
Evaluation: Heterogeneous workloads
FLY-DRAM
VLC
RSC
RLW
Solar-DRAM
Solar-DRAM reduces tRCD for more DRAM accesses
and provides 8.79% performance benefit
Notes: Maybe just remove this slide?

## Slide 48: Temperature
We study the effects of changing temperature on Fprob. The x-axis shows the Fprob at a given temperature T, and the y-axis plots the distribution (box and whiskers plot) of Fprob at a higher temperature for the same bitline
Since a majority of the data points are above the x=y line, Fprob
generally increases with higher temperatures

## Slide 49: Data Pattern Dependence
We study how using different data patterns affects the number of
weak bitlines found over multiple iterations

## Slide 50
DRAM Background
DRAM chips are organized into DRAM ranks and modules.
The CPU interfaces with DRAM at the granularity of a module with a memory controller that has a 64-bit channel connection

## Slide 51
Evaluation Methodology

## Slide 52
Testing Methodology

## Slide 53
Implementation Overhead
The table is stored in the memory controller that interfaces with the DRAM channel