## Slide 1: Application-Aware Memory Channel Partitioning
Sai Prashanth Muralidhara § Lavanya Subramanian †
Onur Mutlu † Mahmut Kandemir §
Thomas Moscibroda ‡
§ Pennsylvania State University † Carnegie Mellon University
‡ Microsoft Research

## Slide 2: Main Memory is a Bottleneck
Main memory latency is long
Core stalls, performance degrades
Multiple applications share the main memory
Main Memory
Core
Core
Core
Memory Controller
Channel

## Slide 3: Problem of Inter-Application Interference
Channel
Main Memory
Core
Core
Memory Controller
Req
Req
Req
Applications’ requests interfere at the main memory
This inter-application interference degrades system performance
Problem further exacerbated due to
  Increasing number of cores
  Limited off-chip pin bandwidth

## Slide 4: Outline
Goal:
Mitigate
Inter-Application Interference
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling

## Slide 5: Background: Main Memory
Row Buffer
Bank 0
Bank 1
Bank 2
Bank 3
Row Buffer
Row Buffer
Row Buffer
Rows
Columns
FR-FCFS memory scheduling policy [Zuravleff et al., US Patent ‘97; Rixner et al., ISCA ‘00]
  Row-buffer hit first
  Oldest request first
Unaware of inter-application interference
Channel
Memory Controller
Bank 0
Bank 1
Bank 2
Bank 3
Row Buffer

## Slide 6: Previous Approach
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling
Previous Approach:
Application-Aware Memory Request Scheduling
Goal:
Mitigate
Inter-Application Interference

## Slide 7: Application-Aware Memory Request Scheduling
Monitor application memory access characteristics
Rank applications based on memory access characteristics
Prioritize requests at the memory controller, based on ranking

## Slide 8: An Example: Thread Cluster Memory Scheduling
thread
Threads in the system
thread
thread
thread
thread
thread
thread
Non-intensive
cluster
Intensive cluster
thread
thread
thread
Memory-non-intensive
Memory-intensive
Prioritized
higher
priority
higher
priority
Throughput
Fairness
Figure: Kim et al., MICRO 2010

## Slide 9: Application-Aware Memory Request Scheduling
Advantages
Reduces interference between applications by
request reordering
Improves system performance
Disadvantages
Requires modifications to memory scheduling logic for
  Ranking
  Prioritization
Cannot completely eliminate interference by request reordering

## Slide 10: Our Approach
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Goal:
Mitigate
Inter-Application Interference

## Slide 11: Observation: Modern Systems Have Multiple Channels
A new degree of freedom
Mapping data across multiple channels
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory

## Slide 12: Data Mapping in Current Systems
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Causes interference between applications’ requests
Page

## Slide 13: Partitioning Channels Between Applications
Channel 0
Red App
Blue App
Memory Controller
Memory Controller
Channel 1
Memory
Core
Core
Memory
Page
Eliminates interference between applications’ requests

## Slide 14: Overview: Memory Channel Partitioning (MCP)
Goal
  Eliminate harmful interference between applications
Basic Idea
  Map the data of badly-interfering applications to different channels
Key Principles
  Separate low and high memory-intensity applications
  Separate low and high row-buffer locality applications

## Slide 15: Key Insight 1: Separate by Memory Intensity
High memory-intensity applications interfere with low memory-intensity applications in shared memory channels
Map data of low and high memory-intensity applications
to different channels
1
2
3
4
5
Channel 0
Bank 1
Channel 1
Bank 0
Conventional Page Mapping
Red App
Blue App
Time Units
Core
Core
Bank 1
Bank 0
Channel Partitioning
Red App
Blue App
Channel 0
Time Units
1
2
3
4
5
Channel 1
Core
Core
Bank 1
Bank 0
Bank 1
Bank 0
Saved Cycles
Saved Cycles

## Slide 16: Key Insight 2: Separate by Row-Buffer Locality
High row-buffer locality applications interfere with low
row-buffer locality applications in shared memory channels
Conventional Page Mapping
Channel 0
Bank 1
Channel 1
Bank 0
R1
R0
R2
R3
R0
R4
Request Buffer State
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Channel 0
R0
R0
Service Order
1
2
3
4
5
6
R2
R3
R4
R1
Time units
Bank 1
Bank 0
Bank 1
Bank 0
R0
Channel 0
R1
R2
R3
R0
R4
Request Buffer State
Channel Partitioning
Bank 1
Bank 0
Bank 1
Bank 0
Channel 1
Saved
Cycles
Map data of low and high row-buffer locality applications to different channels

## Slide 17: Memory Channel Partitioning (MCP) Mechanism
1. Profile applications
2. Classify applications into groups
3. Partition channels between application groups
4. Assign a preferred channel to each application
5. Allocate application pages to preferred channel
Hardware
System Software

## Slide 18: 1. Profile Applications
Hardware counters collect application memory access characteristics
Memory access characteristics
  Memory intensity:
  Last level cache Misses Per Kilo Instruction (MPKI)
  Row-buffer locality:
  Row-buffer Hit Rate (RBH) - percentage of accesses that hit in the row buffer

## Slide 19: 2. Classify Applications
Test MPKI
High Intensity
High
Low
Low Intensity
Test RBH
High Intensity
Low Row-Buffer Locality
Low
High Intensity
High Row-Buffer Locality
High

## Slide 20: 3. Partition Channels Among Groups: Step 1
Channel 1
Assign number of channels proportional to number of applications in group
.
.
.
High Intensity
Low Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
Channel 3
High Intensity
High Row-Buffer Locality

## Slide 21: 3. Partition Channels Among Groups: Step 2
Channel 1
High Intensity
Low Row-Buffer Locality
High Intensity
High Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
.
.
.
Assign number of channels proportional to bandwidth demand of group
Channel 3
Channel 1
.
.
High Intensity
Low Row-Buffer Locality
High Intensity
High Row-Buffer Locality
Low Intensity
Channel 2
Channel N-1
Channel N
Channel N-1
Channel N
Channel 3
.
.
.

## Slide 22: 4. Assign Preferred Channel to Application
Channel 1
Low Intensity
Channel 2
MPKI: 1
MPKI: 3
MPKI: 4
MPKI: 1
MPKI: 3
MPKI: 4
Assign each application a preferred channel from its group’s allocated channels
Distribute applications to channels such that group’s bandwidth demand is balanced across its channels

## Slide 23: 5. Allocate Page to Preferred Channel
Enforce channel preferences computed in the previous step
On a page fault, the operating system
  allocates page to preferred channel if free page available in preferred channel
  if free page not available, replacement policy tries to allocate page to preferred channel
  if it fails, allocate page to another channel

## Slide 24: Interval Based Operation
time
Current Interval
Next Interval
1. Profile applications
2. Classify applications into groups
3. Partition channels between groups
4. Assign preferred channel to applications
5. Enforce channel preferences

## Slide 25: Integrating Partitioning and Scheduling
Previous Approach:
Application-Aware Memory Request Scheduling
Our First Approach:
Application-Aware Memory Channel Partitioning
Our Second Approach: Integrated Memory Partitioning and Scheduling
Goal:
Mitigate
Inter-Application Interference

## Slide 26: Observations
Applications with very low memory-intensity rarely access memory  Dedicating channels to them results in precious memory bandwidth waste
They have the most potential to keep their cores busy  We would really like to prioritize them
They interfere minimally with other applications  Prioritizing them does not hurt others

## Slide 27: Integrated Memory Partitioning and Scheduling (IMPS)
Always prioritize very low memory-intensity applications in the memory scheduler
Use memory channel partitioning to mitigate interference between other applications

## Slide 28: Hardware Cost
Memory Channel Partitioning (MCP)
  Only profiling counters in hardware
  No modifications to memory scheduling logic
  1.5 KB storage cost for a 24-core, 4-channel system
Integrated Memory Partitioning and Scheduling (IMPS)
  A single bit per request
  Scheduler prioritizes based on this single bit

## Slide 29: Methodology
Simulation Model
  24 cores, 4 channels, 4 banks/channel
  Core Model
    Out-of-order, 128-entry instruction window
    512 KB L2 cache/core
  Memory Model – DDR2
Workloads
  240 SPEC CPU 2006 multiprogrammed workloads (categorized based on memory intensity)
Metrics
  System Performance

## Slide 30: Previous Work on Memory Scheduling
FR-FCFS [Zuravleff et al., US Patent 1997, Rixner et al., ISCA 2000]
  Prioritizes row-buffer hits and older requests
  Application-unaware
ATLAS [Kim et al., HPCA 2010]
  Prioritizes applications with low memory-intensity
TCM [Kim et al., MICRO 2010]
  Always prioritizes low memory-intensity applications
  Shuffles request priorities of high memory-intensity applications

## Slide 31: Comparison to Previous Scheduling Policies
1%
5%
Chart: Normalized System Performance
|
FRFCFS | 1
ATLAS | 1.012
TCM | 1.061
MCP | 1.071
IMPS | 1.1108
7%
11%
Significant performance improvement over baseline FRFCFS
Better system performance than the best previous scheduler
at lower hardware cost
Averaged over 240 workloads

## Slide 32: Interaction with Memory Scheduling
Chart: Normalized System Performance
| FRFCFS | ATLAS | TCM
No IMPS | 1 | 1.012 | 1.061
IMPS | 1.1108 | 1.08 | 1.09
Chart: Normalized System Performance
| FRFCFS | ATLAS | TCM
No IMPS | 1 | 1.012 | 1.061

IMPS improves performance regardless of scheduling policy
Highest improvement over FRFCFS as IMPS designed for FRFCFS
Averaged over 240 workloads

## Slide 33: Summary
Uncontrolled inter-application interference in main memory degrades system performance
Application-aware memory channel partitioning (MCP)
  Separates the data of badly-interfering applications to different channels, eliminating interference
Integrated memory partitioning and scheduling (IMPS)
  Prioritizes very low memory-intensity applications in scheduler
  Handles other applications’ interference by partitioning
MCP/IMPS provide better performance than application-aware memory request scheduling at lower hardware cost

## Slide 34: Thank You

## Slide 35: Application-Aware Memory Channel Partitioning
Sai Prashanth Muralidhara § Lavanya Subramanian †
Onur Mutlu † Mahmut Kandemir §
Thomas Moscibroda ‡
§ Pennsylvania State University † Carnegie Mellon University
‡ Microsoft Research

## Slide 36: System Software Overhead
MCP/IMPS require system software to
  Perform preferred channel assignment
  Enforce channel preferences
Preferred channel assignment
  Off the critical path
  Previously computed assignments can be used
Enforcing channel preferences
  Only on a page fault
  N (512) extra entries in circular page list scanned
  Takes less than 10000 extra cycles as compared to baseline page fault time overhead of millions of cycles

## Slide 37: Migration
Less than 12% of all pages in our workloads go to non-preferred channels
When application phase changes
  Application characteristics could change
   Preferred channel could change
  However, we observe working set also changes
   New working set pages allocated to new preferred channel
What to do with the old working set in the old preferred channel?
  Exploring migrating old working set to new channel
  Ideas
    Migrate periodically without hurting demand traffic
    Migrate “hot” (highly accessed) pages

## Slide 38: Effect on Page Faults
MCP/IMPS do not hard partition memory capacity
Replacement policy
  tries to allocate an application’s pages to its preferred channel
  assigns pages to another channel if replacement candidate not found in application’s preferred channel
Das et al., (Safari TR 2011) show that this replacement policy reduces applications’ page fault rates, as it mitigates interference by capacity partitioning

## Slide 39: Different Intensity Categories

## Slide 40: Fairness and System Performance

## Slide 41: Scaling Number of MCs
Chart: Normalized System Performance
| 2.0 | 4.0 | 8.0 | 16.0
FRFCFS | 1 | 1 | 1 | 1
IMPS | 1.16 | 1.17 | 1.14 | 1.07

## Slide 42: Scaling Number of MCs: IMPS bridges the gap
Chart: Normalized System Performance
FRFCFS - 4 MC | 1
MCP - 4 MC | 1.1346
IMPS - 4 MC | 1.1776
FRFCFS - 8 MC | 1.3156
IMPS bridges more than half the gap between 4 and 8 memory controller systems

## Slide 43: Scaling Number of Cores
Chart: Normalized System Performance
| 16.0 | 24.0 | 32.0
FRFCFS | 1 | 1 | 1
IMPS | 1.15 | 1.17 | 1.31

## Slide 44: Scaling Cache Size
Chart: Normalized System Performance
| 256 KB | 512 KB | 1 MB
FRFCFS | 1 | 1 | 1
IMPS | 1.16 | 1.17 | 1.14

## Slide 45: Comparison to Application-Unaware Memory Controller Load Balancing (Awasthi et al., PACT `10)
AFT – Adaptive First Touch, DPM – Dynamic Page Migration –application-unaware load balancing policies
MCP/IMPS outperform AFT and DPM by 7/12.4% respectively (averaged across 40 workloads)
Chart: Normalized System Performance
|
Conv Mapping | 1
AFT | 1.051
DPM | 1.051
MCP | 1.1192
IMPS | 1.1737