## Slide 1
Jawad Haj-Yahya1 Mohammed Alser1 Jeremie Kim1 A. Giray Yaglıkçı1
Nandita Vijaykumar1,2,3 Efraim Rotem2 Onur Mutlu1
SysScale: Exploiting Multi-domain
Dynamic Voltage and Frequency Scaling
for Energy Efficient Mobile Processors
1
3
1
2
Notes: Hi, my name is Jawad Haj-Yahya and I will present our work SysScale: Exploiting Multi-domain Dynamic Voltage and Frequency Scaling for Energy Efficient Mobile Processors

## Slide 2: Overview of a Modern SoC Architecture
IO Interconnect
IO Engines/
Controllers
IO peripherals
Memory
Controller
DDRIO Digital
DDRIO Analog
DRAM
CPU Cores
Last Level
Cache
Graphics
Engines
VDDQ
V_IO
Memory Domain
IO Domain
Compute Domain
V_SA
System On Chip
V_C
V_G
3 domains in modern thermally-constrained mobile SoCs: Compute, Memory, IO
Several voltage sources exist, and some of them are shared between domains
IO controllers and engines, IO interconnect, memory controller, and DDRIO typically each has an independent clock
Compute domain supports dynamic voltage and frequency scaling.
IO and memory domains have fixed clock frequencies and voltages.
Notes: [CLICK]
There are three domains in modern thermally-constrained mobile SoC:
[CLICK]
Compute [CLICK]
Memory [CLICK]
and IO [CLICK]
Several voltage sources exists, and some of them are shared between domains. For example VDDQ [CLICK]
V_IO [CLICK]
V_SA [CLICK]
V_Core [CLICK]
and V_Graphics
[CLICK]
Many components in the SoC normally have their own clock, for example IO controllers and engines, IO interconnect, memory controller, and DDRIO typically each has an independent clock [CLICK]
Compute domain supports dynamic voltage and frequency scaling. [CLICK]
IO and memory domains have fixed clock frequencies and voltages.
[END]

## Slide 3: Our Goal: Holistic SoC Power Management
We conduct a motivational study on a real Intel Broadwell SoC
We conclude that a holistic power management approach is needed to mitigate the power management inefficiencies in current mobile SoCs
Our goal is to provide such an efficient multi-domain power management approach
  by dynamically orchestrating the distribution of the SoC power budget across the three domains based on their actual performance demands
Notes: [CLICK] We conduct a motivational study on a real Intel Broadwell SoC. Based on key observations from this study
[CLICK] We conclude that a holistic power management approach is needed to mitigate the power management inefficiencies in current mobile SoCs [CLICK]
Our goal is to provide such an efficient multi-domain power management approach [CLICK]
  by dynamically orchestrating the distribution of the SoC power budget across the three domains based on their actual performance demands
[END]

## Slide 4: SysScale
SysScale is a new multi-domain power management technique to improve the energy efficiency of mobile SoCs
SysScale is based on three key ideas:
  A new DVFS (dynamic voltage and frequency scaling) mechanism to distribute the SoC power to each domain based on its predicted performance demand
  An accurate algorithm to predict each domain’s performance demand
  Domain-specialized techniques to optimize the energy efficiency of each domain at different operating points
Notes: We propose SysScale [CLICK] SysScale is a new multi-domain power management technique to improve the energy efficiency of mobile SoCs [CLICK]
SysScale is based on three key ideas: [CLICK]
  First, A new DVFS mechanism to distribute the SoC power budget to each domain based on its predicted performance demand [CLICK]
  Secondly, An accurate algorithm to predict each domain’s performance demand [CLICK]
  And finally, Domain-specialized techniques to optimize the energy efficiency of each domain at different operating points.
[END]

## Slide 5: SysScale: Key Results
SysScale is the first work to enable coordinated and highly-efficient DVFS across all SoC domains to increase energy efficiency
SysScale optimizes and efficiently redistributes the total power budget across all SoC domains based on the performance demands of each domain
We implemented SysScale on the Intel Skylake SoC for mobile devices
  SysScale improves the performance of real CPU and graphics workloads (by up to 16% and 8.9%, respectively, for 4.5W TDP)
  SysScale reduces the average power consumption of battery life workloads (by up to 10.7%) across all TDPs of the Intel Skylake system
We show that SysScale is an effective approach to balance power consumption and performance demands across all SoC domains
Notes: [CLICK]
SysScale is the first work to enable coordinated and highly-efficient DVFS across all SoC domains to increase energy efficiency [CLICK]
SysScale optimizes and efficiently redistributes the total power budget across all SoC domains -- based on the performance demands of each domain [CLICK]
We implemented SysScale on the Intel Skylake SoC for mobile devices [CLICK]
  SysScale improves the performance of real CPU and graphics workloads by up to 16% and 8.9% - respectively - for 4.5W Thermal Design Power SoC [CLICK]
  SysScale reduces the average power consumption of battery life workloads by up to 10.7% ---
  across all TDPs of the Intel Skylake system [CLICK]
We show that SysScale is an effective approach to balance power consumption and performance demands across all SoC domains

## Slide 6
Jawad Haj-Yahya1 Mohammed Alser1 Jeremie Kim1 A. Giray Yaglıkçı1
Nandita Vijaykumar1,2,3 Efraim Rotem2 Onur Mutlu1
SysScale: Exploiting Multi-domain
Dynamic Voltage and Frequency Scaling
for Energy Efficient Mobile Processors
1
3
1
2
Notes: Thank you for your attention. For many more details, I invite you to read our ISCA 2020 paper.
[END]