## Slide 1: A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing
Junwhan Ahn, Sungpack Hong*, Sungjoo Yoo, Onur Mutlu+, Kiyoung Choi
Seoul National University
*Oracle Labs
+Carnegie Mellon University

## Slide 2: Graphs
Abstract representation of object relationships
  Vertex: object (e.g., person, article, …)
  Edge: relationship (e.g., friendships, hyperlinks, …)
Recent trend: explosive increase in graph size
36 Million
Wikipedia Pages
1.4 Billion
Facebook Users
300 Million
Twitter Users
30 Billion
Instagram Photos

## Slide 3: Large-Scale Graph Processing
Example: Google’s PageRank
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
for (v: graph.vertices) {
v.rank = v.next_rank; v.next_rank = alpha;
}

## Slide 4: Large-Scale Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
for (v: graph.vertices) {
v.rank = v.next_rank; v.next_rank = alpha;
}
Example: Google’s PageRank
Independent to Each Vertex
Vertex-Parallel Abstraction

## Slide 5: PageRank Performance
Chart: Speedup
| 32 Cores DDR3 | 128 Cores DDR3
열3 | 1 | 1.4206

## Slide 6: Bottleneck of Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…

## Slide 7: Bottleneck of Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
weight * v.rank
v
w
&w
1. Frequent random memory accesses
2. Little amount of computation
w.rank
w.next_rank
w.edges
…
High Memory Bandwidth Demand

## Slide 8: PageRank Performance
Chart: Speedup
| 32 Cores DDR3 | 128 Cores DDR3
열3 | 1 | 1.4206
(102.4GB/s)
(102.4GB/s)

## Slide 9: PageRank Performance
Chart: Speedup
| 32 Cores DDR3 | 128 Cores DDR3 | 128 Cores HMC
열3 | 1 | 1.4206 | 1.8907
(102.4GB/s)
(102.4GB/s)
(640GB/s)

## Slide 10: PageRank Performance
Chart: Speedup
| 32 Cores DDR3 | 128 Cores DDR3 | 128 Cores HMC
열3 | 1 | 1.4206 | 1.8907
(102.4GB/s)
(102.4GB/s)
(640GB/s)

## Slide 11: PageRank Performance
Chart: Speedup
| 32 Cores DDR3 | 128 Cores DDR3 | 128 Cores HMC | 128 Cores HMC Internal BW
열3 | 1 | 1.4206 | 1.8907 | 5.2517
(102.4GB/s)
(102.4GB/s)
(640GB/s)
(8TB/s)
Lessons Learned:
High memory bandwidth is the key to the scalability of graph processing
Conventional systems do not fully utilize high memory bandwidth

## Slide 12: Challenges in Scalable Graph Processing
Challenge 1: How to provide high memory bandwidth to computation units in a practical way?
  Processing-in-memory based on 3D-stacked DRAM
Challenge 2: How to design computation units that efficiently exploit large memory bandwidth?
  Specialized in-order cores called Tesseract cores
    Latency-tolerant programming model
    Graph-processing-specific prefetching schemes

## Slide 13: Tesseract System
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)

## Slide 14: Tesseract System
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)

## Slide 15: Tesseract System
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Communications via Remote Function Calls

## Slide 16: Communications in Tesseract
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
v
w
&w

## Slide 17: Communications in Tesseract
for (v: graph.vertices) {
for (w: v.successors) {
w.next_rank += weight * v.rank;
}
}
w
Vault #1
Vault #2
v
&w

## Slide 18: Communications in Tesseract
for (v: graph.vertices) {
for (w: v.successors) {
put(w.id, function() { w.next_rank += weight * v.rank; });
}
}
barrier();
Can be delayed until the nearest barrier
w
Vault #1
Vault #2
put
put
put
put
v
&w
Non-blocking Remote Function Call

## Slide 19: Non-blocking Remote Function Call
Local
Core
NI
Remote
Core
NI
&func, &w, value
Send function address & args to the remote core
Store the incoming message to the message queue
Flush the message queue when it is full or a synchronization barrier is reached
put(w.id, function() { w.next_rank += value; })
MQ

## Slide 20: Benefits of Non-blocking Remote Function Call
Latency hiding through fire-and-forget
  Local cores are not blocked by remote function calls
Localized memory traffic
  No off-chip traffic during remote function call execution
No need for mutexes
  Non-blocking remote function calls are atomic
Prefetching
  Will be covered shortly

## Slide 21: Tesseract System
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)

## Slide 22: Tesseract System
Crossbar Network
…
…
…
…
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
LP
Host Processor
Memory-Mapped
Accelerator Interface
(Noncacheable, Physically Addressed)
Prefetching

## Slide 23: Memory Access Patterns in Graph Processing
for (v: graph.vertices) {
for (w: v.successors) {
put(w.id, function() { w.next_rank += weight * v.rank; });
}
}
w
Vault #1
Vault #2
v
&w
Sequential
(Local)
Random (Remote)

## Slide 24: Message-Triggered Prefetching
Prefetching random memory accesses is difficult
Opportunities in Tesseract
  Domain-specific knowledge of target data address
  Time slack of non-blocking remote function calls
for (v: graph.vertices) {
for (w: v.successors) {
put(w.id, function() { w.next_rank += weight * v.rank; });
}
}
barrier();
Can be delayed
until the nearest barrier

## Slide 25: Message-Triggered Prefetching
DRAM Controller
NI
put(w.id, function() { w.next_rank += value; })
In-Order Core
Message Queue
MTP
PF Buffer

## Slide 26: Message-Triggered Prefetching
DRAM Controller
NI
In-Order Core
Message Queue
MTP
put(w.id, function() { w.next_rank += value; }, &w.next_rank)
PF Buffer

## Slide 27: Message-Triggered Prefetching
Message M1 received
Request prefetch
Mark M1 as ready when the prefetch is serviced
DRAM Controller
NI
In-Order Core
Message Queue
MTP
put(w.id, function() { w.next_rank += value; }, &w.next_rank)
M1

PF Buffer
w.next..

## Slide 28: Message-Triggered Prefetching
Message M1 received
Request prefetch
Mark M1 as ready when the prefetch is serviced
Process multiple ready messages at once
DRAM Controller
NI
In-Order Core
Message Queue
PF Buffer
MTP
put(w.id, function() { w.next_rank += value; }, &w.next_rank)
d1
M4
d2
d3
M1

M2

M3


## Slide 29: Other Features of Tesseract
Blocking remote function calls
List prefetching
Prefetch buffer
Programming APIs
Application mapping
Please see the paper for details

## Slide 30: Evaluated Systems
HMC-MC
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
128 In-Order
2GHz
102.4GB/s
640GB/s
640GB/s
8TB/s
HMC-OoO
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
(with FDP)
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
8 OoO
4GHz
DDR3-OoO
(with FDP)
Tesseract
32 Tesseract Cores
(32-entry MQ, 4KB PF Buffer)

## Slide 31: Workloads
Five graph processing algorithms
  Average teenage follower
  Conductance
  PageRank
  Single-source shortest path
  Vertex cover
Three real-world large graphs
  ljournal-2008 (social network)
  enwiki-2003 (Wikipedia)
  indochina-0024 (web graph)
  4~7M vertices, 79~194M edges

## Slide 32: Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814

## Slide 33: Performance
Chart: Speedup
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 1 | 1.5592 | 1.2525 | 9.0241 | 11.6257 | 13.7814
Chart: Memory Bandwidth Consumption
| DDR3-OoO | HMC-OoO | HMC-MC | Tesseract | Tesseract- LP | Tesseract- LP-MTP
계열 1 | 0.079545 | 0.1904 | 0.24289 | 1.2943 | 2.244 | 2.9197

## Slide 34: Iso-Bandwidth Comparison
Chart: Speedup
| HMC-MC | HMC-MC + PIM BW | Tesseract + Conventional BW | Tesseract
계열 1 | 1 | 2.3043 | 3.0224 | 6.4999
HMC-MC Bandwidth (640GB/s)
Tesseract Bandwidth (8TB/s)
Bandwidth
Programming Model
(No Prefetching)

## Slide 35: Execution Time Breakdown
Chart: 
| AT.LJ | CT.LJ | PR.LJ | SP.LJ | VC.LJ
Normal Mode | 30.9935 | 37.7468 | 31.6792 | 61.1137 | 52.7933
Interrupt Mode | 16.4807 | 40.1271 | 30.6682 | 9.5699 | 14.9513
Interrupt Switching | 10.6891 | 5.5968 | 6.7038 | 6.274 | 4.1054
Network | 26.8961 | 5.9297 | 20.5682 | 8.9943 | 15.0048
Barrier | 14.9405 | 10.5996 | 10.3807 | 14.0482 | 13.1452

## Slide 36: Execution Time Breakdown
Chart: 
| AT.LJ | CT.LJ | PR.LJ | SP.LJ | VC.LJ
Normal Mode | 30.9935 | 37.7468 | 31.6792 | 61.1137 | 52.7933
Interrupt Mode | 16.4807 | 40.1271 | 30.6682 | 9.5699 | 14.9513
Interrupt Switching | 10.6891 | 5.5968 | 6.7038 | 6.274 | 4.1054
Network | 26.8961 | 5.9297 | 20.5682 | 8.9943 | 15.0048
Barrier | 14.9405 | 10.5996 | 10.3807 | 14.0482 | 13.1452
Network Backpressure due to Message Passing
(Future work: message combiner, …)

## Slide 37: Execution Time Breakdown
Chart: 
| AT.LJ | CT.LJ | PR.LJ | SP.LJ | VC.LJ
Normal Mode | 30.9935 | 37.7468 | 31.6792 | 61.1137 | 52.7933
Interrupt Mode | 16.4807 | 40.1271 | 30.6682 | 9.5699 | 14.9513
Interrupt Switching | 10.6891 | 5.5968 | 6.7038 | 6.274 | 4.1054
Network | 26.8961 | 5.9297 | 20.5682 | 8.9943 | 15.0048
Barrier | 14.9405 | 10.5996 | 10.3807 | 14.0482 | 13.1452
Workload Imbalance
(Future work: load balancing)

## Slide 38: Prefetch Efficiency
Chart: Prefetch Timeliness
| Tesseract with Prefetching | Ideal
열1 | 1 | 1.0358
Chart: Coverage
| Prefetch Buffer Hit | Demand L1 Miss
계열 1 | 0.87529 | 0.12471
(Prefetch takes zero cycles)

## Slide 39: Scalability
Chart: Tesseract with Prefetching
| 32 Cores | 128 Cores | 512 Cores | 512 Cores + Partitioning
계열 1 | 1 | 3.957 | 11.9791 | 13.2508
Chart: DDR3-OoO
| 32 Cores | 128 Cores
열3 | 1 | 1.4206
(8GB)
(32GB)
(128GB)
Memory-Capacity-Proportional Performance

## Slide 40: Memory Energy Consumption
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
-87%

## Slide 41: Memory Energy Consumption
Chart: 
| HMC-OoO | Tesseract with Prefetching
Memory Layers | 0.063751 | 0.024336
Logic Layers | 0.93625 | 0.08992
Cores | 0 | 0.020219
-87%
Chart: 
| Memory Layers | Logic Layers | Cores
열1 | 0.024336 | 0.08992 | 0.020219

## Slide 42: Conclusion
Revisiting the PIM concept in a new context
  Cost-effective 3D integration of logic and memory
  Graph processing workloads demanding high memory bandwidth
Tesseract: scalable PIM for graph processing
  Many in-order cores in a memory chip
  New message passing mechanism for latency hiding
  New hardware prefetchers for graph processing
  Programming interface that exploits our hardware design
Evaluations demonstrate the benefits of Tesseract
  14x performance improvement & 87% energy reduction
  Scalable: memory-capacity-proportional performance

## Slide 43: A Scalable Processing-in-Memory Accelerator for Parallel Graph Processing
Junwhan Ahn, Sungpack Hong*, Sungjoo Yoo, Onur Mutlu+, Kiyoung Choi
Seoul National University
*Oracle Labs
+Carnegie Mellon University