## Slide 1
Energy-Efficient Data Compression for GPU Memory Systems
Gennady Pekhimenko (Advisors: Todd C. Mowry and Onur Mutlu) – Carnegie Mellon University
High Performance Computing is Everywhere
Memory systems are bandwidth constrained
Energy efficiency is key across the board
Data Compression is a promising technique to address these challenges
Applications today are data-intensive
Potential for HW-Based Data Compression
Multiple simple patterns: zeros, repeated values, narrow values, pointers (low dynamic range)
Different Compression Algorithms:
  BΔI [PACT’12] is based on Base-Delta Encoding
  Frequent Pattern Compression (FPC) [ISCA’04]
  C-Pack [Trans. on VLSI’12]
  Statistical Compression (SC2) [ISCA’14]
These algorithms improve performance
But there are challenges…
Energy Efficiency: What is a Bit “Toggle”?
0011
Previous data:
How energy is spent in data transfers:
0101
New data:
Energy = CV2 + Fixed
Toggles are expensive
Excessive Bit Toggles with Data Compression
0x00003A00
Uncompressed Cache Line
0x8001D000
0x00003A01
0x8001D008
0x5 0x3A00
Compressed Cache Line (FPC)
0x7 8001D000
0x5 0x3A01
0x7 8001D008
0x00003A00
0x8001D000
Flit 0
0x00003A01
0x8001D008
Flit 1
XOR
..0000001…00001000
# Toggles = 2
5 3A00 7 8001D000 5 1D
Flit 0
1 01 7 8001D008 5 3A02 1
Flit 1
XOR
001001111…10100011000
# Toggles = 31
Toggle-Aware Energy-Efficient Data Compression
Problem:
+ 1.53X effective compression ratio
- 2.19X increase in toggle count
Goal:
Find the optimal tradeoff between
toggle count and compression ratio
Key Idea – Energy Control (EC):
Determine toggle count
Use a heuristic (Energy X Delay and
Energy X Delay2 metrics)
Throttle compression when needed
Optimization: Metadata Consolidation (MC)
0x5 0x3A00 0x5 0x3A01
Compressed Cache Line (FPC)
0x5 0x3A02 0x5 0x3A03
Metadata
…
0x3A00 0x3A01
Metadata Consolidation (MC)
0x3A02 0x3A03
0x5 0x5 … 0x5
Consolidated
Metadata
# Toggles = 18
# Toggles = 2
MC
EC efficiently trades compressibility with toggles
MC reduces toggles & preserves compression ratio
Energy Control (EC)
Initial Results: Compression Ratio and Toggle Rate
Chart: Normalized Toggle #
| FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | Discrete | Mobile
Base | 1.1884 | 1.1267 | 1.1487 | 1.2039 | 1.1993 | 1.1116 | 1.0919 | 2.1276 | 2.1399 | 1.8349 | 1.9797 | 2.1896
EC | 1.0382 | 1.0284 | 1.0494 | 1.0565 | 1.009 | 1.047 | 1.0021 | 1.0345 | 1.0352 | 1.2366 | 1.1484 | 1.1513
Chart: Compression Ratio
| FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | LZSS | Fibonacci | C-Pack | Discrete | Mobile
Base | 1.2773 | 1.2912 | 1.3721 | 1.3496 | 1.2468 | 1.4379 | 1.0061 | 1.2549 | 1.2557 | 1.5255 | 1.5687 | 1.4733
EC | 1.2653 | 1.2793 | 1.3631 | 1.3285 | 1.2174 | 1.419 | 1.0034 | 1.1321 | 1.1324 | 1.4436 | 1.4144 | 1.3154
Applications from NVIDIA: Mobile GPU – 54 in total, Discrete GPU – 167 in total
MC Results:
3.2%/2.9% reduction in toggles for FPC/C-Pack
Future Work:
Detailed Power/Energy model
Effect on different layers in memory hierarchy (DRAM and NoCs)
EC significantly reduces the number of toggles
EC preserves most of the compression benefits