## Slide 1: Understanding Latency Variation in Modern DRAM Chips Experimental Characterization, Analysis, and Optimization
Kevin Chang Abhijith Kashyap, Hasan Hassan, Saugata Ghose, Kevin Hsieh, Donghyuk Lee, Tianshi Li, Gennady Pekhimenko, Samira Khan, Onur Mutlu
v1.3

## Slide 2: Main Memory Latency Lags Behind
Chart: Improvement
| 1999.0 | 2003.0 | 2006.0 | 2008.0 | 2011.0 | 2013.0 | 2014.0 | 2015.0
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275
64x
16x
1.2x
Long DRAM latency → performance bottleneck
In-memory DB, Spark, JVM, … [Clapp+ (Intel), IISWC’15]
Google warehouse-scale workloads [Kanev+ (Google), ISCA’15]

## Slide 3: Why is Latency High?
DRAM latency: Delay as specified in DRAM standards
  Doesn’t reflect true DRAM device latency
Imperfect manufacturing process → latency variation
High standard latency chosen to increase yield
High
Low
DRAM Latency
DRAM A
DRAM B
DRAM C
Manufacturing Variation
Standard
Latency

## Slide 4: Goals
1 Understand and characterize latency variation in modern DRAM chips
2 Develop a mechanism that exploits latency variation to reduce DRAM latency
1
2

## Slide 5: Outline
Motivation and Goals
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Flexible-Latency DRAM
Conclusion

## Slide 6: High-Level DRAM Organization
DRAM
Channel
DIMM
(Dual in-line memory module)
DRAM
chip

## Slide 7: DRAM Chip Internals
DRAM Cell
Row Buffer
…
…
…
8KB (128 cache lines)

## Slide 8: DRAM Operations
ACTIVATE: Store the row into the row buffer
READ: Select the target cache line and drive to CPU
PRECHARGE: Prepare the array for a new ACTIVATE
1
1
1
1
1
2
3
to CPU

## Slide 9: DRAM Timing Parameters
Command
Data
Duration
ACTIVATE
READ
PRECHARGE
1
1
1
1
Cache line (64B)
Next
ACT
Activation latency: tRCD (13ns / 50 cycles)
1
Precharge latency: tRP (13ns / 50 cycles)
2

## Slide 10: DRAM Latency Variation
High
Low
DRAM Latency
DRAM B
DRAM A
DRAM C
Imperfect manufacturing process → latency variation
Slow cells

## Slide 11: Experimental Questions
Can we show latency variation in these parameters?
Can we identify the properties of slow cells with long latency?
Can we isolate slow cells to make DRAM faster?
Imperfect manufacturing process → latency variation
How large is latency variation in modern DRAM chips?

## Slide 12: Experimental Methodology
Tool that enables us to freely issue DRAM commands
  Existing systems: Commands are generated and controlled by HW
Custom FPGA-based infrastructure
PCIe
DDR3
PC
FPGA
DIMM
C++ programs to specify commands
Generate
command sequence

## Slide 13: Experiments
Swept each timing parameter to read data
  Time step of 2.5ns (FPGA cycle time)
Quantified timing errors: bit flips when using reduced latency
Tested 240 DDR3 DRAM chips from three vendors
  30 DIMMs
  Manufacturing dates: 2011 – 2013
  Capacity: 1GB
  Ambient temperature: 20oC

## Slide 14: Outline
Motivation and Goals
DRAM Background
Experimental Methodology
Characterization Results
  Activation latency
  Precharge latency
Mechanism: Flexible-Latency DRAM
Conclusion

## Slide 15: Activation Latency: Key Observation
1
1
1
1
1
?
?
1
First read after ACT
0
1
1
Second read w/ sufficient activation time
Command
ACTIVATE
READ
READ
Actual ACT Time
X
Observation: ACT errors are isolated in the cells read in the first cache line
Row Buffer
Not fully activated
tRCD

## Slide 16: Variation in Activation Errors
Different characteristics across DIMMs
No ACT Errors
Results from 7500 rounds over 240 chips
Very few errors
Modern DRAM chips exhibit significant variation in activation latency
Rife w/ errors
13.1ns
standard
Many errors
Max
Min
Quartiles

## Slide 17: Spatial Locality of Activation Errors
Activation errors are concentrated at certain columns of cells
One DIMM @ tRCD=7.5ns

## Slide 18: Strong Pattern Dependence
DIMM A
DIMM B
DIMM C
Row buffer design is biased towards 1 over 0 [Lim+, ISSCC’12]
Activation errors have a strong dependence on the stored data patterns
> 4 orders of magnitude

## Slide 19: Precharge Latency: Key Observation
Observation: PRE errors occur in multiple cache lines in the row activated after a precharge
Command
PRECHARGE
Actual PRE Time
ACTIVATE
Row Buffer
Incorrectly sensed data
1
1
1
1
1
1
1
1
Not fully precharged
0
0
0
0
0
0
tRP

## Slide 20: Variation in Precharge Errors
No PRE Errors
Few errors
Results from 4000 rounds over 240 chips
Rife w/ errors
Different characteristics across DIMMs
Modern DRAM chips exhibit significant variation in precharge latency
13.1ns
standard
Many errors

## Slide 21: Spatial Locality of Precharge Errors
Precharge errors are concentrated at certain rows of cells
One DIMM @ tRP=7.5ns

## Slide 22: Outline
Motivation and Goals
DRAM Background
Experimental Methodology
Characterization Results
Mechanism: Flexible-Latency DRAM
Conclusion

## Slide 23: Mechanism to Reduce DRAM Latency
Observations
  DRAM timing errors are concentrated on certain regions
  All cells operate without errors at 10ns tRCD and tRP
Flexible-LatencY (FLY) DRAM
  A software-transparent design that reduces latency
Key idea:
  1) Divide memory into regions of different latencies
  2) Memory controller: Use lower latency for regions without slow cells; higher latency for other regions

## Slide 24: FLY-DRAM Evaluation Methodology
Cycle-level simulator: Ramulator [CAL’15] https://github.com/CMU-SAFARI/ramulator
8-core system with DDR3 memory
Benchmarks: SPEC2006, TPC, STREAM, random
  40 8-core workloads
Performance metric: Weighted Speedup (WS)

## Slide 25: FLY-DRAM Configurations
Chart: Fraction of Cells
| Baseline (DDR3) | D1 | D2 | D3 | Upper Bound
7.5ns | 0 | 13 | 74 | 99 | 100
10ns | 0 | 87 | 26 | 1 | 0
13ns | 100 | 0 | 0 | 0 | 0
Chart: Fraction of Cells
| Baseline (DDR3) | D1 | D2 | D3 | Upper Bound
7.5ns | 0 | 12 | 93 | 99 | 100
10ns | 0 | 88 | 7 | 1 | 0
13ns | 100 | 0 | 0 | 0 | 0
Profiles of 3 real DIMMs
12%
93%
99%
13%
74%
99%
tRCD
tRP

## Slide 26: Results
Chart: 40 Workloads
Baseline (DDR3) | 1
FLY-DRAM (D1) | 1.133
FLY-DRAM (D2) | 1.176
FLY-DRAM (D3) | 1.195
Upper Bound | 1.197
17.6%
19.5%
19.7%
13.3%
FLY-DRAM improves performance by exploiting latency variation in DRAM

## Slide 27: Other Results in the Paper
Error-correcting codes (ECC)
  Effective at correcting activation errors
Restoration latency
  Significant margin to complete without errors
Effect of temperature
  Difference is not statistically significant to draw conclusion

## Slide 28: Conclusion
First to experimentally demonstrate and analyze latency variation behavior within real DRAM chips
Show across 240 DRAM chips that:
  All cells work below standard latency
  Some regions of cells work even faster, but slow cells in other regions start to fail
  Error rate is data-dependent
FLY-DRAM reduces latency by using low latency for regions without slow cells and high latency for others
  13%/17%/19% speedup based on profiles of 3 real DIMMs
https://github.com/CMU-SAFARI/DRAM-Latency-Variation-Study

## Slide 29: Understanding Latency Variation in Modern DRAM Chips Experimental Characterization, Analysis, and Optimization
Kevin Chang Abhijith Kashyap, Hasan Hassan, Saugata Ghose, Kevin Hsieh, Donghyuk Lee, Tianshi Li, Gennady Pekhimenko, Samira Khan, Onur Mutlu

## Slide 30: Backup Slides

## Slide 31: Infrastructure
Temperature Controller
Heater
FPGA
DIMM

## Slide 32: DRAM DIMMs

## Slide 33: Activation Latency Variation by DRAM Models

## Slide 34: Activation Errors in Data Bursts

## Slide 35: Effect of ECC on Activation Errors

## Slide 36: Activation Errors by Temperature

## Slide 37: Precharge Latency Variation by DRAM Models