## Slide 1: Row Buffer Locality Aware Caching Policies for Hybrid Memories
HanBin Yoon
Justin Meza
Rachata Ausavarungnirun Rachael Harding
Onur Mutlu
Notes: Hello. I’ll be presenting Row Buffer Locality Aware Caching Policies for Hybrid Memories.
My name is HanBin Yoon and this work has been done together with Justin Meza, Rachata Ausavarungnirun, Rachael Harding, and Onur Mutlu.

## Slide 2: Executive Summary
Different memory technologies have different strengths
A hybrid memory system (DRAM-PCM) aims for best of both
Problem: How to place data between these heterogeneous memory devices?
Observation: PCM array access latency is higher than DRAM’s – But peripheral circuit (row buffer) access latencies are similar
Key Idea: Use row buffer locality (RBL) as a key criterion for data placement
Solution: Cache to DRAM rows with low RBL and high reuse
Improves both performance and energy efficiency over state-of-the-art caching policies
Notes: Here’s a one-slide summary of what I’ll describe.
Different memory technologies have different strengths and weaknesses.
A hybrid memory system, for example, one that combines DRAM and Phase Change Memory, aims for the best of both memory technologies.
The Problem is how to place data between these heterogeneous devices in a way that exploits each memory technology’s strengths while minimizing its weaknesses.
Our key observation is that PCM array access latency is higher than DRAM’s, but peripheral circuit access latencies, or what is called row buffer access latencies, are similar.
Our key idea is to use row buffer locality as a key criterion for data placement in a hybrid memory system.
Our solution is to cache to DRAM rows with low row buffer locality and high reuse because these are the rows that would benefit most from DRAM.
This improves both performance and energy efficiency over state-of-the-art caching policies for hybrid memories.

## Slide 3: Demand for Memory Capacity
1. Increasing cores and thread contexts
  Intel Sandy Bridge: 8 cores (16 threads)
  AMD Abu Dhabi: 16 cores
  IBM POWER7: 8 cores (32 threads)
  Sun T4: 8 cores (64 threads)
Notes: The demand for memory capacity is increasing.
There are two trends that are fueling this demand.
The first is the increasing number of cores and thread contexts on modern chip multiprocessor systems. These systems can execute multiple parallel programs, which results in a large aggregate working set size in memory.
The second is the modern data-intensive applications that operate on large datasets, such as graph, database, and scientific workloads. Such applications benefit from large memory capacities.

## Slide 4: Demand for Memory Capacity
1. Increasing cores and thread contexts
  Intel Sandy Bridge: 8 cores (16 threads)
  AMD Abu Dhabi: 16 cores
  IBM POWER7: 8 cores (32 threads)
  Sun T4: 8 cores (64 threads)
2. Modern data-intensive applications operate on increasingly larger datasets
  Graph, database, scientific workloads
Notes: The demand for memory capacity is increasing.
There are two trends that are fueling this demand.
The first is the increasing number of cores and thread contexts on modern chip multiprocessor systems. These systems can execute multiple parallel programs, which results in a large aggregate working set size in memory.
The second is the modern data-intensive applications that operate on large datasets, such as graph, database, and scientific workloads. Such applications benefit from large memory capacities.

## Slide 5: Emerging High Density Memory
DRAM density scaling becoming costly
Promising: Phase change memory (PCM)
  + Projected 3−12 denser than DRAM [Mohan HPTS’09]
  + Non-volatile data storage
However, cannot simply replace DRAM
  − Higher access latency (4−12 DRAM) [Lee+ ISCA’09]
  − Higher dynamic energy (2−40 DRAM) [Lee+ ISCA’09]
  − Limited write endurance (108 writes) [Lee+ ISCA’09]
 Employ both DRAM and PCM
Notes: Emerging high density memory technologies are becoming a scalable alternative to DRAM, whose density scaling is becoming more and more costly.
Phase change memory, or PCM, is an example of one promising emerging memory technology, which we will focus on.
PCM is projected to be 3 to 12 times denser than DRAM.
It is also a non-volatile data storage medium, which provides two benefits: One is that the data will persist in the absence of power, and the second is that it does not expend refresh energy.
However, we cannot simply replace DRAM with PCM, because of PCM’s higher access latency, higher dynamic energy, and limited write endurance.
For this reason, previous work has looked at employing both DRAM and PCM in the memory system.

## Slide 6: Hybrid Memory
Benefits from both DRAM and PCM
  DRAM: Low latency, dyn. energy, high endurance
  PCM: High capacity, low static energy (no refresh)
DRAM
PCM
CPU
MC
MC
Notes: We call such a memory system a hybrid memory system.
A DRAM-PCM hybrid memory system aims to benefit from both DRAM and PCM’s strengths.
Those would be for DRAM: its low latency, low dynamic energy, and high endurance.
For PCM, its strengths are its high capacity and low static energy.
Here we see a pictorial representation of a DRAM-PCM hybrid memory system.

## Slide 7: Hybrid Memory
Design direction: DRAM as a cache to PCM [Qureshi+ ISCA’09]
  Need to avoid excessive data movement
  Need to efficiently utilize the DRAM cache
DRAM
PCM
CPU
MC
MC
Notes: Previous work has looked at using DRAM as a cache to PCM.
However, moving large amounts of data between DRAM and PCM can cause flood the memory system.

## Slide 8: Hybrid Memory
Key question: How to place data between the heterogeneous memory devices?
DRAM
PCM
CPU
MC
MC
Notes: One key question in the design of a hybrid memory system is: How to place data between the heterogeneous memory devices?
Our goal in this work is to answer this question.

## Slide 9: Outline
Background: Hybrid Memory Systems
Motivation: Row Buffers and Implications on Data Placement
Mechanisms: Row Buffer Locality-Aware Caching Policies
Evaluation and Results
Conclusion
Notes: Here’s the outline for the talk.
I’ve talked about some background in hybrid memory systems.
Next I will talk about row buffers and their implications on data placement.

## Slide 10: Hybrid Memory: A Closer Look
MC
MC
DRAM
(small capacity cache)
PCM (large capacity store)
CPU
Memory channel
Bank
Bank
Bank
Bank
Row buffer
Notes: Here’s a closer look at a hybrid memory system employing both DRAM and PCM.
Typically, the DRAM is used as a small capacity cache, and the PCM is used as a large capacity store.
When the processor needs data, it will first look to see if the data is in DRAM. If the data is indeed in DRAM, the processor will retrieve the data from there. If the data is not in DRAM, the processor will retrieve the data from PCM.
Both DRAM and PCM are organized into banks that are capable of operating independently. Also, in each bank, there are peripheral circuitries known as the row buffers.

## Slide 11: Row Buffers and Latency
Row (buffer) hit: Access data from row buffer  fast
Row (buffer) miss: Access data from cell array  slow
LOAD X
LOAD X+1
LOAD X+1
LOAD X
ROW ADDRESS
ROW DATA
Row buffer miss!
Row buffer hit!
Bank
Row buffer
CELL ARRAY
Notes: Row buffers affect memory latency is a profound way.
Row buffers effectively store the most recently accessed row in memory.
They are typically 2 to 8KB in length, for a single rank.
When data is requested in memory, it is first checked to see if the data is in the row buffer. If the data is not in the row buffer, this is called a row buffer miss. In this case, we need to read a row full of data from the memory cell array into the row buffer, and the memory request is served. In a subsequent memory request, if the requested data is already latched in the row buffer, this is called a row buffer hit, and the data can be retrieved without having to access the memory cell array, which in the case of PCM, is a high latency operation.
In summary, on a row hit, data is accessed from the row buffer, which is fast. On a row miss, data is accessed from the cell array, which is slow.

## Slide 12: Key Observation
Row buffers exist in both DRAM and PCM
  Row hit latency similar in DRAM & PCM [Lee+ ISCA’09]
  Row miss latency small in DRAM, large in PCM
Place data in DRAM which
  is likely to miss in the row buffer (low row buffer locality) miss penalty is smaller in DRAM
  AND
  is reused many times  cache only the data worth the movement cost and DRAM space
Notes: Our key observation is that row buffers exist in both DRAM and PCM.
Row hit latency, which does not access the memory cell array, is similar in DRAM and PCM.
It is for a row miss that the memory access latency is small in DRAM and large in PCM.
Therefore we would like to place data in DRAM which:
Is likely to miss in the row buffer, which we call as having low row buffer locality, since the row buffer miss penalty is small in DRAM than it is in PCM.
And we would like to place data in DRAM which is reused many times, so that we cache only the data that is worth the movement cost.

## Slide 13: RBL-Awareness: An Example
Let’s say a processor accesses four rows
Row A
Row B
Row C
Row D
Notes: Let’s look at an example how row buffer locality affects hybrid memory performance.
Let’s say a processor accesses four rows…

## Slide 14: RBL-Awareness: An Example
Let’s say a processor accesses four rows with different row buffer localities (RBL)
Row A
Row B
Row C
Row D
Low RBL
(Frequently miss
in row buffer)
High RBL
(Frequently hit
in row buffer)
Case 1: RBL-Unaware Policy (state-of-the-art)
Case 2: RBL-Aware Policy (RBLA)
Notes: With different row buffer localities.
Rows A and B have low row buffer locality, which means that they frequently miss in the row buffer, and rows C and D have high row buffer locality, which means that they frequently hit in the row buffer.
We will look at two types of caching policies: Case 1 will be row buffer locality unaware, and case 2 will be row buffer locality aware.

## Slide 15: Case 1: RBL-Unaware Policy
A row buffer locality-unaware policy could
place these rows in the following manner
DRAM (High RBL)
PCM (Low RBL)
Row C
Row D
Row A
Row B
Notes: Here’s Case 1: The row buffer locality unaware policy.
A row buffer locality unaware policy could place rows A, B, C, and D in the following manner, where rows with high row buffer locality are placed in DRAM, and rows with low row buffer locality are placed in PCM.

## Slide 16: Case 1: RBL-Unaware Policy
RBL-Unaware: Stall time is 6 PCM device accesses
DRAM (High RBL)
PCM (Low RBL)
A
B
C
D
C
C
D
D
A
B
A
B
Access pattern to main memory:
A (oldest), B, C, C, C, A, B, D, D, D, A, B (youngest)
time
Notes: For such a policy, this diagram shows the amount of time it takes to serve a stream of memory requests.
This is the access pattern to memory.
Clearly, the high row buffer miss latency of PCM acts as a bottleneck to serving all of the memory requests, and this happens because the rows with low row buffer locality is placed in PCM.

## Slide 17: Case 2: RBL-Aware Policy (RBLA)
A row buffer locality-aware policy would place these rows in the opposite manner
DRAM (Low RBL)
PCM (High RBL)
 Access data at lower row buffer miss latency of DRAM
 Access data at low row buffer hit latency of PCM
Row A
Row B
Row C
Row D
Notes: Here’s Case 2: The row buffer locality aware policy, or RBLA.
A row buffer locality aware policy would place these rows in the following manner, where the rows with low row buffer locality are placed in DRAM, since the data can be accessed at the lower row buffer miss latency of DRAM.
Rows with high row buffer locality will be placed in PCM, since data can be frequently accessed at the low row buffer hit latency of PCM.

## Slide 18: Case 2: RBL-Aware Policy (RBLA)
Saved cycles
DRAM (High RBL)
PCM (Low RBL)
A
B
C
D
C
C
D
D
A
B
A
B
Access pattern to main memory:
A (oldest), B, C, C, C, A, B, D, D, D, A, B (youngest)
DRAM (Low RBL)
PCM (High RBL)
time
A
B
C
D
C
C
D
D
A
B
A
B
RBL-Unaware: Stall time is 6 PCM device accesses
RBL-Aware: Stall time is 6 DRAM device accesses
Notes: Now we compare the two policies in terms of the time it takes to serve the same stream of memory requests.
Remember, this was the timeline shown before for the row buffer locality-unaware policy.
For case 2, the row buffer locality aware policy, although the PCM row buffer miss latency is high, many of the accesses to PCM are row buffer hit accesses that can be served quickly.
And overall, it takes less time to serve all of the memory requests in the row buffer locality aware policy.
The row buffer locality aware policy gains because it places rows with low row buffer locality in DRAM.
This is the goal of our mechanism: To place rows with low row buffer locality in DRAM.

## Slide 19: Outline
Background: Hybrid Memory Systems
Motivation: Row Buffers and Implications on Data Placement
Mechanisms: Row Buffer Locality-Aware Caching Policies
Evaluation and Results
Conclusion
Notes: Now I will talk about how we do that.

## Slide 20: Our Mechanism: RBLA
For recently used rows in PCM:
  Count row buffer misses as indicator of row buffer locality (RBL)
Cache to DRAM rows with misses  threshold
  Row buffer miss counts are periodically reset (only cache rows with high reuse)
Notes: Our Mechanism is called RBLA, which stands for row buffer locality aware.
For recently used rows in PCM, our mechanism counts row buffer misses as indicator of row buffer locality of each row.
I will talk more about how this is physically achieved.
Then, we cache to DRAM rows with row buffer miss counts that exceed a certain threshold.
And row buffer miss counts are periodically reset, so that we only cache rows with high reuse.
That is our base mechanism, RBLA.

## Slide 21: Our Mechanism: RBLA-Dyn
For recently used rows in PCM:
  Count row buffer misses as indicator of row buffer locality (RBL)
Cache to DRAM rows with misses  threshold
  Row buffer miss counts are periodically reset (only cache rows with high reuse)
Dynamically adjust threshold to adapt to workload/system characteristics
  Interval-based cost-benefit analysis
Notes: We also extend RBLA to RBLA-Dyn, which performs an extra step.
RBLA-Dyn dynamically adjusts the threshold value to adapt to different workload and system characteristics.
This is based on an interval-based cost-benefit analysis, for which the details can be found in the paper.
I would encourage you to read the paper, and I’d be happy to answer any questions.

## Slide 22: Implementation: “Statistics Store”
Goal: To keep count of row buffer misses to recently used rows in PCM
Hardware structure in memory controller
  Operation is similar to a cache
    Input: row address
    Output: row buffer miss count
  128-set 16-way statistics store (9.25KB) achieves system performance within 0.3% of an unlimited-sized statistics store
Notes: The implementation of our mechanism requires a statistics store, or what we simply call a stats store.
The goal of the stats store is to keep count of the row buffer misses to recently used rows in PCM.
The stats store is a hardware structure in the memory controller, and its operation is similar to a cache.
It is organized into sets and ways, and is indexed using the row address of the row we wish to find the row buffer miss count for.
If the queried row is currently in the stats store, then its row buffer miss count will be output.
We find that a 128-set 16-way stats store, 9.25KB in size, achieves system performance within 0.3% of an unlimited-sized stats store.

## Slide 23: Outline
Background: Hybrid Memory Systems
Motivation: Row Buffers and Implications on Data Placement
Mechanisms: Row Buffer Locality-Aware Caching Policies
Evaluation and Results
Conclusion
Notes: Now let’s take a look at our results.

## Slide 24: Evaluation Methodology
Cycle-level x86 CPU-memory simulator
  CPU: 16 out-of-order cores, 32KB private L1 per core, 512KB shared L2 per core
  Memory: 1GB DRAM (8 banks), 16GB PCM (8 banks), 4KB migration granularity
36 multi-programmed server, cloud workloads
  Server: TPC-C (OLTP), TPC-H (Decision Support)
  Cloud: Apache (Webserv.), H.264 (Video), TPC-C/H
Metrics: Weighted speedup (perf.), perf./Watt (energy eff.), Maximum slowdown (fairness)
Notes: Here’s our evaluation methodology.
We use a cycle-level x86 simulator to test our hybrid memory caching policies.
We simulate a 16-core system with 1GB of DRAM and 16GB of PCM.
We use 36 multi-programmed server and cloud workloads to test our caching policies.
For server workloads, we use TPC-C, which is an online transaction processing benchmark, and TPC-H, which is a decision support benchmark.
For cloud workloads, we use Apache, which is a webserver application, and H.264, a video processing application, as well as TPC-C and H.
We report multi-core performance in terms of weighted speedup, multi-core fairness in terms of maximum slowdown, and energy efficiency in terms of performance per Watt.

## Slide 25: Comparison Points
Conventional LRU Caching
FREQ: Access-frequency-based caching
  Places “hot data” in cache [Jiang+ HPCA’10]
  Cache to DRAM rows with accesses  threshold
  Row buffer locality-unaware
FREQ-Dyn: Adaptive Freq.-based caching
  FREQ + our dynamic threshold adjustment
  Row buffer locality-unaware
RBLA: Row buffer locality-aware caching
RBLA-Dyn: Adaptive RBL-aware caching
Notes: And here are our comparison points.
The standard conventional LRU caching caches any row from PCM to DRAM when the data is touched. We find this scheme to generate too much data movement between DRAM and PCM and consequently to not perform well. So we’re not going to use it as a comparison point in this talk.
Frek is access frequency based caching. It is inspired by prior work that selectively caches hot data.
The downsides of frek is that it is row buffer locality aware. Hence, it would place a row with high row buffer locality in DRAM, although that row may be accessed as efficiently in PCM.
Frek-Dyn augments frek with the adaptive threshold adjustment technique.
It has the same drawback as frek, in that it is row buffer locality unaware.
Our mechanisms, RBLA and RBLA-Dyn, are specifically designed to be aware of row buffer locality and to exploit it.

## Slide 26: System Performance
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.9552 | 1.0469 | 1
FREQ-Dyn | 1.0502 | 1.1074 | 1.0784
RBLA | 1.0713 | 1.0997 | 1.0854
RBLA-Dyn | 1.1204 | 1.1511 | 1.1356
10%
14%
Benefit 1: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM
17%
Benefit 1: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM
Benefit 2: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 2: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 3: Balanced memory request load between DRAM and PCM
Notes: Here are the system performance results of the different hybrid memory caching policies.
RBLA-Dyn achieves 17% performance improvement over frek in server workloads, 10% in cloud, and 14% overall.
This is due to a number of reasons.
The first is that RBLA-Dyn increases row buffer locality in PCM by moving low row buffer locality data to DRAM.
The second is that RBLA-Dyn reduces memory bandwidth consumption due its stricter caching criteria.
And RBLA-Dyn also has the effect of balancing the memory request load between DRAM and PCM by letting rows with high row buffer locality remain in PCM, instead of fetching all accessed data to DRAM.

## Slide 27: Average Memory Latency
Chart: Workload
| Server | Cloud | Avg
FREQ | 1.1028 | 0.9068 | 1
FREQ-Dyn | 1.0156 | 0.85733 | 0.9331
RBLA | 1.0006 | 0.8704 | 0.93324
RBLA-Dyn | 0.94644 | 0.82222 | 0.88214
14%
9%
12%
Notes: These benefits are also reflected in the average memory latency, which RBLA-Dyn reduces by 14% over frek in server workloads, by 9% in cloud, and by 12% overall.

## Slide 28: Memory Energy Efficiency
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.99688 | 1.0031 | 1
FREQ-Dyn | 1.0786 | 1.0475 | 1.0629
RBLA | 1.0901 | 1.0386 | 1.064
RBLA-Dyn | 1.1281 | 1.0731 | 1.1002
Increased performance & reduced data movement between DRAM and PCM
7%
10%
13%
Notes: RBLA-Dyn improves memory system energy efficiency by 13% in server workloads, 7% in cloud, and 10% overall.
This is partly due to the increased system performance, and partly due to the reduced data movement between DRAM and PCM because of RBLA-Dyn’s stricter caching criteria.

## Slide 29: Thread Fairness
Chart: Workload
| Server | Cloud | Avg
FREQ | 1.1145 | 0.89726 | 1
FREQ-Dyn | 1.0492 | 0.87701 | 0.95924
RBLA | 1.0703 | 0.86925 | 0.96457
RBLA-Dyn | 1.0303 | 0.85386 | 0.93795
7.6%
4.8%
6.2%
Notes: And our mechanism also improves multi-core thread fairness by 7.6% in server workloads, by 4.8% in cloud, and by 6.2% overall.

## Slide 30: Compared to All-PCM/DRAM
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Chart: Normalized Weighted Speedup
| Avg
16GB PCM | 1
RBLA-Dyn | 1.3108
16GB DRAM | 1.8423
Chart: Normalized Max. Slowdown
| Avg
16GB PCM | 1
RBLA-Dyn | 0.81719
16GB DRAM | 0.56921
Our mechanism achieves 31% better performance than all PCM, within 29% of all DRAM performance
31%
29%
Notes: Now let’s compare our mechanism to a homogeneous memory system.
Here the comparison points are a 16GB all-PCM and all-DRAM memory system.
Our mechanism achieves 31% better performance than the all-PCM memory system, and comes within 29% of the all-DRAM performance.
Note that we do not assume any capacity benefits of PCM over DRAM.
And yet, our mechanism bridges the performance gap between the two homogeneous memory systems.
If the capacity benefit of PCM was included, the hybrid memory system will perform even better.

## Slide 31: Other Results in Paper
RBLA-Dyn increases the portion of PCM row buffer hit by 6.6 times
RBLA-Dyn has the effect of balancing memory request load between DRAM and PCM
  PCM channel utilization increases by 60%.
Notes: Here’s a highlight of our other results in the paper.
RBLA-Dyn increases the portion of PCM row buffer hit accesses significantly.
It has the effect of balancing memory request load between DRAM and PCM.

## Slide 32: Summary
Different memory technologies have different strengths
A hybrid memory system (DRAM-PCM) aims for best of both
Problem: How to place data between these heterogeneous memory devices?
Observation: PCM array access latency is higher than DRAM’s – But peripheral circuit (row buffer) access latencies are similar
Key Idea: Use row buffer locality (RBL) as a key criterion for data placement
Solution: Cache to DRAM rows with low RBL and high reuse
Improves both performance and energy efficiency over state-of-the-art caching policies
Notes: Here’s a one-slide summary of what I’ll describe.
Different memory technologies have different strengths and weaknesses.
A hybrid memory system, for example, one that combines DRAM and Phase Change Memory, aims for the best of both memory technologies.
The Problem is how to place data between these heterogeneous devices in a way that exploits each memory technology’s strengths while minimizing its weaknesses.
Our key observation is that PCM array access latency is higher than DRAM’s, but peripheral circuit access latencies, or what is called row buffer access latencies, are similar.
Our key idea is to use row buffer locality as a key criterion for data placement in a hybrid memory system.
Our solution is to cache to DRAM rows with low row buffer locality and high reuse because these are the rows that would benefit most from DRAM.
This improves both performance and energy efficiency over state-of-the-art caching policies for hybrid memories.

## Slide 33: Thank you! Questions?
Notes: Thank you! And I’ll take questions.

## Slide 34: Row Buffer Locality Aware Caching Policies for Hybrid Memories
HanBin Yoon
Justin Meza
Rachata Ausavarungnirun Rachael Harding
Onur Mutlu

## Slide 35: Appendix

## Slide 36: Cost-Benefit Analysis (1/2)
Each quantum, we measure the first-order costs and benefits under the current threshold
  Cost = cycles expended for data movement
  Benefit = cycles saved servicing requests in DRAM versus PCM
Cost = Migrations × tmigration
Benefit = ReadsDRAM × (tread,PCM − tread,DRAM) + WritesDRAM × (twrite,PCM − twrite,DRAM)

## Slide 37: Cost-Benefit Analysis (2/2)
Dynamic Threshold Adjustment Algorithm
NetBenefit = Benefit - Cost
if (NetBenefit < 0)
MissThresh++
else if (NetBenefit > PreviousNetBenefit)
if (MissThresh was previously incremented)
MissThresh++
else
MissThresh--
else
if (MissThresh was previously incremented)
MissThresh--
else
MissThresh++
PreviousNetBenefit = NetBenefit

## Slide 38: Simulator Parameters
Core model
  3-wide issue with 128-entry instruction window
  Private 32 KB per core L1 cache
  Shared 512 KB per core L2 cache
Memory model
  1 GB DRAM (1 rank), 16 GB PCM (1 rank)
  Separate memory controllers, 8 banks per device
  Row buffer hit: 40 ns
  Row buffer miss: 80 ns (DRAM); 128, 368 ns (PCM)
  Migrate data at 4 KB granularity

## Slide 39: Row Buffer Locality
Chart: Workload
| Server | Cloud | Avg
DRAM row hit | 0 | 0 | 0
DRAM row miss | 0 | 0 | 0
PCM row hit | 0 | 0 | 0
PCM row miss | 0 | 0 | 0
Chart: 
| Server | Cloud | Avg
RCM RBM | 0.0207 | 0.015 | 0.0182
DRAM RBM | 0.6034 | 0.7329 | 0.6739
PCM RBH | 0.0165 | 0.0105 | 0.0131
DRAM RBH | 0.3594 | 0.2417 | 0.2947
Chart: 
| Server | Cloud | Avg
RCM RBM | 0.0629 | 0.0519 | 0.0615
DRAM RBM | 0.6089 | 0.7389 | 0.6792
PCM RBH | 0.0829 | 0.0387 | 0.0566
DRAM RBH | 0.3496 | 0.2379 | 0.2884
Chart: 
| Server | Cloud | Avg
RCM RBM | 0.0222 | 0.0171 | 0.0271
DRAM RBM | 0.6328 | 0.7521 | 0.6981
PCM RBH | 0.1413 | 0.0615 | 0.0932
DRAM RBH | 0.3428 | 0.2302 | 0.2809
Chart: 
| Server | Cloud | Avg
RCM RBM | 0.0531 | 0.0537 | 0.0601
DRAM RBM | 0.6347 | 0.7558 | 0.7008
PCM RBH | 0.1647 | 0.0814 | 0.1158
DRAM RBH | 0.3445 | 0.2317 | 0.2826
FREQ
FREQ-Dyn
RBLA
RBLA-Dyn

## Slide 40: PCM Channel Utilization
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.10761 | 0.064042 | 0.083014
FREQ-Dyn | 0.16023 | 0.092194 | 0.12154
RBLA | 0.15487 | 0.081862 | 0.1126
RBLA-Dyn | 0.17435 | 0.10163 | 0.13311
Notes: And our mechanism also improves multi-core thread fairness by 7.6% in server workloads, by 4.8% in cloud, and by 6.2% overall.

## Slide 41: DRAM Channel Utilization
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.61902 | 0.57527 | 0.59674
FREQ-Dyn | 0.61005 | 0.57057 | 0.58998
RBLA | 0.604 | 0.56928 | 0.58638
RBLA-Dyn | 0.59528 | 0.56182 | 0.57831
Notes: And our mechanism also improves multi-core thread fairness by 7.6% in server workloads, by 4.8% in cloud, and by 6.2% overall.

## Slide 42: Compared to All-PCM/DRAM
Chart: Normalized Metric
| Weighted Speedup | Max. Slowdown | Perf. per Watt
16GB PCM | 1 | 1 | 1
RBLA-Dyn | 1.3108 | 0.81719 | 0.46542
16GB DRAM | 1.8423 | 0.56921 | 0.44307
Notes: And our mechanism also improves multi-core thread fairness by 7.6% in server workloads, by 4.8% in cloud, and by 6.2% overall.

## Slide 43: Memory Lifetime
Chart: Workload
| Server | Cloud | Avg
16GB PCM | 0.39501 | 0.46642 | 0.42923
FREQ-Dyn | 7.5362 | 20.9644 | 12.5695
RBLA-Dyn | 5.0477 | 9.4219 | 6.8963
Notes: And our mechanism also improves multi-core thread fairness by 7.6% in server workloads, by 4.8% in cloud, and by 6.2% overall.

## Slide 44: DRAM Cache Hit Rate
Chart: Workload
| Server | Cloud | Avg
FREQ | 0.96278 | 0.97457 | 0.96866
FREQ-Dyn | 0.86794 | 0.91516 | 0.89123
RBLA | 0.85651 | 0.92596 | 0.89056
RBLA-Dyn | 0.81805 | 0.87968 | 0.84831
Notes: And our mechanism also improves multi-core thread fairness by 7.6% in server workloads, by 4.8% in cloud, and by 6.2% overall.